Part 2 - "INFORMATION SECURITY"

## Note 1	Not used since 2015

Note 2	Category 5 – Part 2 does not apply to products when accompanying their user for the user's personal use.

Note 3	Cryptography Note

5.A.2., 5.D.2.a.1., 5.D.2.b. and 5.D.2.c.1. do not apply to items as follows:

a.	Items meeting all of the following:

1.	Generally available to the public by being sold, without restriction, from stock at retail selling points by means of any of the following:

a.	Over-the-counter transactions;

b.	Mail order transactions;

c.	Electronic transactions; or

d.	Telephone call transactions;

2.	The cryptographic functionality cannot easily be changed by the user;

3.	Designed for installation by the user without further substantial support by the supplier; and

4.	When necessary, details of the items are accessible and will be provided, upon request, to the appropriate authority in the exporter's country in order to ascertain compliance with conditions described in paragraphs 1. to 3. above;

b.	Hardware components or 'executable software', of existing items described in paragraph a. of this Note, that have been designed for these existing items, and meeting all of the following:

1.	"Information security" is not the primary function or set of functions of the component or 'executable software';

2.	The component or 'executable software' does not change any cryptographic functionality of the existing items, or add new cryptographic functionality to the existing items;

3.	The feature set of the component or 'executable software' is fixed and is not designed or modified to customer specification; and

4.	When necessary as determined by the appropriate authority in the exporter’s country, details of the component or 'executable software', and details of relevant end-items are accessible and will be provided to the authority upon request, in order to ascertain compliance with conditions described above.

Technical Note

For the purpose of the Cryptography Note, 'executable software' means "software" in executable form, from an existing hardware component excluded from 5.A.2. by the Cryptography Note.

Note	'Executable software' does not include complete binary images of the "software" running on an end-item.

Note to the Cryptography Note:

1.	To meet paragraph a. of Note 3, all of the following must apply:

a.	The item is of potential interest to a wide range of individuals and businesses; and

b.	The price and information about the main functionality of the item are available before purchase without the need to consult the vendor or supplier.  A simple price enquiry is not considered to be a consultation.

2.	In determining eligibility of paragraph a. of Note 3, national authorities may take into account relevant factors such as quantity, price, required technical skill, existing sales channels, typical customers, typical use or any exclusionary practices of the supplier.

5.	A.	Part 2.	SYSTEMS, EQUIPMENT AND COMPONENTS

# CRYPTOGRAPHIC "INFORMATION SECURITY"

5.	A.	2.	"Information security" systems, equipment and components, as follows:

N.B.	For Global Navigation Satellite Systems (GNSS) receiving equipment containing or employing decryption see 7.A.5., and for related decryption "software" and "technology" see 7.D.5. and 7.E.1.

a.	Designed or modified to use 'cryptography for data confidentiality' having 'in excess of 56 bits of symmetric key length, or equivalent', where that cryptographic capability is usable without "cryptographic activation" or has been activated, as follows:

1.	Items having "information security" as a primary function;

2.	Digital communication or networking systems, equipment or components, not specified in paragraph 5.A.2.a.1.;

3.	Computers, other items having information storage or processing as a primary function, and components therefor, not specified in paragraphs 5.A.2.a.1. or 5.A.2.a.2.;

N.B.	For operating systems, see also 5.D.2.a.1. and 5.D.2.c.1.

4.	Items, not specified in paragraphs 5.A.2.a.1. to a.3., where the 'cryptography for data confidentiality' having 'in excess of 56 bits of symmetric key length, or equivalent' meets all of the following:

a.	It supports a non-primary function of the item; and

b.	It is performed by incorporated equipment or "software" that would, as a standalone item, be specified by Category 5 – Part 2.

Technical Notes

- For the purposes of 5.A.2.a., 'cryptography for data confidentiality’ means “cryptography” that employs digital techniques and performs any cryptographic function other than any of the following:

  - "Authentication";

  - Digital signature;

  - Data integrity;

  - Non-repudiation;

  - Digital rights management, including the execution of copy-protected "software";

  - Encryption or decryption in support of entertainment, mass commercial broadcasts or medical records management; or

  - Key management in support of any function described in paragraph a. to f. above.

Technical Notes cont.

- For the purposes of 5.A.2.a., 'in excess of 56 bits of symmetric key length, or equivalent' means any of the following:

  - A "symmetric algorithm" employing a key length in excess of 56 bits, not including parity bits; or

  - An "asymmetric algorithm" where the security of the algorithm is based on any of the following:

    - Factorisation of integers in excess of 512 bits (e.g., RSA);

    - Computation of discrete logarithms in a multiplicative group of a finite field of size greater than 512 bits (e.g., Diffie-Hellman over Z/pZ); or

    - Discrete logarithms in a group other than mentioned in paragraph b.2. in excess of 112 bits (e.g., Diffie-Hellman over an elliptic curve).

Note 1	When necessary as determined by the appropriate authority in the exporter's country, details of items must be accessible and provided to the authority upon request, in order to establish any of the following:

- Whether the item meets the criteria of 5.A.2.a.1. to a.4.; or

- Whether the cryptographic capability for data confidentiality specified by 5.A.2.a. is usable without "cryptographic activation".

Note 2	5.A.2.a. does not apply to any of the following items, or specially designed "information security" components therefor:

a.	Smart cards and smart card 'readers/writers' as follows:

1.	A smart card or an electronically readable personal document (e.g., token coin, e-passport) that meets any of the following:

a.	The cryptographic capability meets all of the following:

1.	It is restricted for use in any of the following:

a.	Equipment or systems not described by 5.A.2.a.1. to a.4.;

b.	Equipment or systems not using 'cryptography for data confidentiality' having 'in excess of 56 bits of symmetric key length, or equivalent'; or

c.	Equipment or systems excluded from 5.A.2.a. by entries b. to f. of this Note; and

2.	It cannot be reprogrammed for any other use; or

b.	Having all of the following:

1.	It is specially designed and limited to allow protection of 'personal data' stored within;

2.	Has been, or can only be, personalized for public or commercial transactions or individual identification; and

3.	Where the cryptographic capability is not user-accessible;

Note 2 cont.

Technical Note

'Personal data' includes any data specific to a particular person or entity, such as the amount of money stored and data necessary for "authentication".

2.	'Readers/writers' specially designed or modified, and limited, for items specified by paragraph a.1. of this Note;

Technical Note

'Readers/writers' include equipment that communicates with smart cards or electronically readable documents through a network.

b.	Cryptographic equipment specially designed and limited for banking use or 'money transactions';

Technical Note

'Money transactions' in 5.A.2. Note 2.b. includes the collection and settlement of fares or credit functions.

c.	Portable or mobile radiotelephones for civil use (e.g., for use with commercial civil cellular radio communication systems) that are not capable of transmitting encrypted data directly to another radiotelephone or equipment (other than Radio Access Network (RAN) equipment), nor of passing encrypted data through RAN equipment (e.g., Radio Network Controller (RNC) or Base Station Controller (BSC));

d.	Cordless telephone equipment not capable of end-to-end encryption where the maximum effective range of unboosted cordless operation (i.e., a single, unrelayed hop between terminal and home base station) is less than 400 metres according to the manufacturer's specifications;

e.	Portable or mobile radiotelephones and similar client wireless devices for civil use, that implement only published or commercial cryptographic standards (except for anti-piracy functions, which may be non-published) and also meet the provisions of paragraphs a.2. to a.4. of the Cryptography Note (Note 3 in Category 5 – Part 2), that have been customised for a specific civil industry application with features that do not affect the cryptographic functionality of these original non-customised devices;

f.	Items, where the “information security” functionality is limited to wireless "personal area network" functionality, meeting all of the following:

1.	Implement only published or commercial cryptographic standards; and

2.	The cryptographic capability is limited to a nominal operating range not exceeding 30 metres according to the manufacturer’s specifications, or not exceeding 100 metres according to the manufacturer’s specifications for equipment that cannot interconnect with more than seven devices;

Note 2 cont.

g.	Mobile telecommunications Radio Access Network (RAN) equipment designed for civil use, which also meet the provisions of paragraphs a.2. to a.4. of the Cryptography Note (Note 3 in Category 5 – Part 2), having an RF output power limited to 0.1W (20 dBm) or less, and supporting 16 or fewer concurrent users;

h.	Routers, switches or relays, where the "information security" functionality is limited to the tasks of "Operations, Administration or Maintenance" ("OAM") implementing only published or commercial cryptographic standards; or

i.	General purpose computing equipment or servers, where the "information security" functionality meets all of the following:

1.	Uses only published or commercial cryptographic standards; and

2.	Is any of the following:

a.	Integral to a CPU that meets the provisions of Note 3 in Category 5 – Part 2;

b.	Integral to an operating system that is not specified by 5.D.2.; or

c.	Limited to "OAM" of the equipment.

5.	A.	2.	b.	Designed or modified to enable, by means of "cryptographic activation", an item to achieve or exceed the controlled performance levels for functionality specified by 5.A.2.a. that would not otherwise be enabled;

c.	Designed or modified to use or perform "quantum cryptography";

# Technical Note

# "Quantum cryptography" is also known as Quantum Key Distribution (QKD).

d.	Designed or modified to use cryptographic techniques to generate channelising codes, scrambling codes or network identification codes, for systems using ultra-wideband modulation techniques and having any of the following:

- A bandwidth exceeding 500 MHz; or

- A "fractional bandwidth" of 20% or more;

e.	Designed or modified to use cryptographic techniques to generate the spreading code for "spread spectrum" systems, not specified by 5.A.2.d., including the hopping code for "frequency hopping" systems.

# NON-CRYPTOGRAPHIC "INFORMATION SECURITY"

5.	A.	3.	Systems, equipment and components, for non-cryptographic "information security", as follows:

a.	Communications cable systems designed or modified using mechanical, electrical or electronic means to detect surreptitious intrusion;

Note	5.A.3.a. applies only to physical layer security.  For the purpose of 5.A.3.a., the physical layer includes Layer 1 of the Reference Model of Open Systems Interconnection (OSI) (ISO/IEC 7498-1).

b.	Specially designed or modified to reduce the compromising emanations of information-bearing signals beyond what is necessary for health, safety or electromagnetic interference standards.

# DEFEATING, WEAKENING OR BYPASSING "INFORMATION SECURITY"

5.	A.	4.	Systems, equipment and components for defeating, weakening or bypassing "information security", as follows:

a.	Designed or modified to perform 'cryptanalytic functions'.

Note	5.A.4.a. includes systems or equipment, designed or modified to perform 'cryptanalytic functions' by means of reverse engineering.

# Technical Note

# 'Cryptanalytic functions' are functions designed to defeat cryptographic mechanisms in order to derive confidential variables or sensitive data, including clear text, passwords or cryptographic keys.

5.	B.	Part 2.	TEST, INSPECTION AND PRODUCTION EQUIPMENT

5.	B.	2.	"Information security" test, inspection and "production" equipment, as follows:

a.	Equipment specially designed for the "development" or "production" of equipment specified by 5.A.2., 5.A.3., 5.A.4. or 5.B.2.b.;

b.	Measuring equipment specially designed to evaluate and validate the "information security" functions of equipment specified by 5.A.2., 5.A.3. or 5.A.4., or of "software" specified by 5.D.2.a. or 5.D.2.c.

5.	C.	Part 2.	MATERIALS - None

5.	D.	Part 2.	SOFTWARE

5.	D.	2.	"Software" as follows:

a.	"Software" specially designed or modified for the "development", "production" or "use" of any of the following:

1.	Equipment specified by 5.A.2. or "software" specified by 5.D.2.c.1.;

2.	Equipment specified by 5.A.3. or "software" specified by 5.D.2.c.2.; or

3.	Equipment specified by 5.A.4. or "software" specified by 5.D.2.c.3.;

b.	"Software" designed or modified to enable, by means of "cryptographic activation", an item to meet the criteria for functionality specified by 5.A.2.a., that would not otherwise be met;

c.	"Software" having the characteristics of, or performing or simulating the functions of, any of the following:

1.	Equipment specified by 5.A.2.a., 5.A.2.c., 5.A.2.d. or 5.A.2.e.;

Note	5.D.2.c.1. does not apply to "software" limited to the tasks of "OAM" implementing only published or commercial cryptographic standards.

2.	Equipment specified by 5.A.3.; or

3.	Equipment specified by 5.A.4.

d.	Not used since 2016

N.B.	See 5.D.2.b. for items formerly specified in 5.D.2.d.

5.	E.	Part 2.	TECHNOLOGY

5.	E.	2.	"Technology" as follows:

a.	"Technology" according to the General Technology Note for the "development", "production" or "use" of equipment specified by 5.A.2., 5.A.3., 5.A.4. or 5.B.2., or of "software" specified by 5.D.2.a. or 5.D.2.c.;

b.	"Technology" to enable, by means of "cryptographic activation", an item to meet the criteria for functionality specified by 5.A.2.a., that would not otherwise be met.

Note	5.E.2. includes "information security" technical data resulting from procedures carried out to evaluate or determine the implementation of functions, features or techniques specified in Category 5 – Part 2.