Technical Specification:

XML for Hotel Availability

(OTA release 2005a)

Revisions

| Date | Description |  |
| --- | --- | --- |
| 06/25/04 | Modified /ACT mapping in Availability Request and Integrated Availability Request to use a “RequestType” element within the “TPA_Extensions” element to define the type of XML request. | William Metz |
| 06/25/04 | Modified /BSA and /BSM mapping in Availability Request to show the use of the RequestorID element, not the UniqueID element. | William Metz |
| 06/25/04 | Updated XML examples to validate against OTA 2003A published schemas. Changed schema references in all XML examples. Changed “MembershipId” attribute of “CustLoyalty” element to be “MembershipID” in the Availability request example. Added “TPA_Extensions/RequestType” element to Availability and Integrated Availability request examples. Removed “SummaryOnly” attribute from Availability Request example. | William Metz |
| 08/11/04 | Added /TOC and /NCH mapping for request messages | William Metz |
| 09/20/04 | Added comment to /CXP mapping for Source Availability response | William Metz |
| 9/21/04 | Added ‘local hotel time and day of arrival to the ‘A’ and ‘P’ for the /CXP field in the Associate Avail Response to Worldspan | Sharon Thomas |
| 9/27/05 | Added the two new slash data fields /LVL and /SPC and the OTA mapping examples to the Availability Response grid and sample messages. ONLY the Source Avail Response has new OPTIONAL fields. The Availability request is not changing. | Sharon Thomas |
| 11/3/05 | Added new Hotel Source Availability response indicators ‘T’ (rate includes taxes and surcharges) and ‘B’ (breakfast included in rate). | Sharon Thomas |
| 12/29/05 | Added new ‘X’ rate plan code | Sharon Thomas |
| 1/18/06 | Modified /PC and /CD fields to accommodate 1-8 occurrences. Formerly limited to a maximum of 3. | Sharon Thomas |
| 1/18/06 | Reorganized the order of the /IND rate indicators. | Sharon Thomas |
| 07/11/06 07/26/06 | Updated specification: Added a new column,XML Field Length Removed Worldspan Bedding Type Codes; Pg.9 Replaced OTA_ Hotel AvailRQ and RS example with a new example; Pg.9 Removed ‘NET’, LVLX references Dates changed to show current year | Sue Blunt |
| 08/08/06 | Added /RCU Recurring Currency field to document | Sue Blunt |
| 08/16/06 | /IND inbound response field added ‘X’ to show as TPF field /IND slash data response examples | Sue Blunt |
| 08/25/06 | Added response fld lengths starting at /CUR | Sue Blunt |
| 11/16/06 | Added ‘s’ to the XML OTA element name AvailRequestSegment; now showing in all instances, AvailRequestSegments | Sue Blunt |
|  | Added OTA equivalent codes to the WSP codes for attribute, RoomViewCode;Pg.7 |  |
| 11/17/06 | Added OTA equivalent codes to the WSP codes for attribute, RoomViewCode;Pg.7 | Sue Blunt |
| 11/28/06 | Formatting changes; | Sue Blunt |

Table of Contents

I. AVAILABILITY REQUEST (message from Worldspan to associate)	4

OTA XML Availability Request Format:	10

Worldspan Availability Request Slash Data Examples:	11

II. AVAILABILITY RESPONSE (from Associate to Worldspan):	12

OTA XML Availability Response Format:	18

OTA XML Availability Response Format: (Error Response - AVLERR)	19

Example Hotel Source Availability Responses from Hotel Associate to Worldspan:	20

## I. AVAILABILITY REQUEST (message from Worldspan to associate)

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
|  | EchoToken These field IDs are part of EchoToken string 1-64 | 6 | X | Session Number (6 numeric) Worldspan fixed length 6 bytes | OTA_HotelAvailRQ EchoToken=”000006#1P# 42251C#AB345#AV” |
| /COM |  | 2 | X | Partition identifier(alphanumeric or alpha/numeric) Worldspan fixed length 2 bytes | OTA_HotelAvailRQ EchoToken=”000006#1P# 42251C#AB345#AV” |
| /LNI |  | 6 | X | Agents LNIATA(alpha/numeric) Worldspan fixed length 6 bytes | OTA_HotelAvailRQ EchoToken=”000006#1P# 42251C#AB345#AV” |
| /SQN |  | 5 | X | Worldspan sequence number(alpha/numeric) Worldspan fixed length 5 bytes | OTA_HotelAvailRQ EchoToken=”000006#1P# 42251C#AB345#AV” |
| /SYS | NMToken | 1 | X | Worldspan processing indicator Worldspan fixed length 1 byte ’Test’ or ‘Production’ | OTA_HotelAvailRQ Target=”Production” |
| /ACT | Variable TPA Extension | 3 | X | Request Type AV=Availability | OTA_HotelAvailRQ EchoToken=”000006#1P# 42251C#AB345#AV”> <AvailRequestSegments> <AvailRequestSegment> <TPA_Extensions > <RequestType>AV</RequestType> |
| /CHN | 1-8 | 3 | X | Hotel Chain Code Worldspan fixed length 3 bytes | <AvailRequestSegments> <AvailRequestSegment> <HotelSearchCriteria> <Criterion> <HotelRef ChainCode=”XX” > |
| /CTY | 1-8 | 3 |  | Hotel City Worldspan fixed length 3 bytes | <AvailRequestSegments> <AvailRequestSegment> <HotelSearchCriteria> <Criterion> <HotelRef HotelCityCode=”CHI” > |
| /PID | 1-16 | 5 | X | Property Code Worldspan maximum length 5 bytes | <AvailRequestSegments> <AvailRequestSegment> <HotelSearchCriteria> <Criterion> <HotelRef HotelCode=”12345” |
| /CKI | 25 | 5 | X | Check-in date YYYY-MM-DD Note: While OTA accepts 25 characters in this field the 10 byte, format Is YYYY-MM-DD. | <AvailRequestSegments> <AvailRequestSegment> <StayDateRange Start=”2006-09-21”/> |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /CKO | 25 | 5 | X | Check-out Date YYYY-MM-DD Note: While OTA accepts 25 characters in this field the 10 byte, format Is YYYY-MM-DD. | <AvailRequestSegments> <AvailRequestSegment> <StayDateRange End=”2006-09-21”/> |
| /NPR | 999 | 1 | X | Number of persons Worldspan fixed length 1 byte | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate> <GuestCounts IsPerRoom=”1”> <GuestCount Count=”2”/> |
| /TOC | TPA Extention | 2 |  | Total occupants sharing room / accommodation Worldspan maximum length 2 bytes | <AvailRequestSegments> <AvailRequestSegment> <TPA_Extensions> <TotalOccupants>5</TotalOccupants></TPA_Extensions> |
| /NCH | TPA Extention | 2 |  | Number of children sharing room / accommodation Worldspan maximum length 2 bytes | <AvailRequestSegments> <AvailRequestSegment> <TPA_Extensions> <NumberOfChildren>2</NumberOfChildren> </TPA_Extensions> |
| /NRM | 999 | 1 | X | Number of rooms requested Worldspan fixed length 1 byte | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate Quantity=”1”/> |
| /LVL | Rate Plan Type (RPT) If present, the OTA code will be translated into the WSP 1-byte alpha code | 1 |  | Rate Plan code/level Worldspan maximum length 1 byte 1-byte rate plan codes may be sent May repeat up to 5 occurrences OTA code equivalent to the WSP code 13 = A-Rack General 14 = S-Senior Citizen 4 = C-Corporate 15 = T-Tour 8 = G-Government 3 = V-Convention 16 = I-Travel Agent Rates 11 = K-Package 17 = W-Weekend 9 = M-Military 10 = N-Negotiated/Secured 5 = Z-Day Rate 12 = P-Promotional | <AvailRequestSegments> <AvailRequestSegment> <RatePlanCandidates> <RatePlanCandidate RatePlanType= ”4”/> <RatePlanCandidate RatePlanType= ”12”/> <RatePlanCandidate RatePlanType= ”14”/> |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /CID | 1-16 1-32 | 20 |  | Corporate ID input by agency (manual input) Worldspan maximum length 20 bytes for membership ID See OTA code table for ProfileType values (ProfileType “1” = Customer) | <AvailRequestSegments> <AvailRequestSegment> < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”CID” MembershipID=”1234567”/> |
| /PC# | 64 There is no equivalent OTA Code to WSP Code If /LVL = N; Set RatePlanType to “10“ | 3 |  | Plan Code and a number from 1-8. May occur a maximum of 8 times. Worldspan fixed length 3 bytes 10=Negotiated | <RatePlanCandidates> <RatePlanCandidate> RatePlanType=”10” RatePlanCode= ”AMX ”/> |
| /CD# | 64 | 20 |  | Corporate ID and a number from 1-8 Worldspan maximum length 20 bytes Associated to a corresponding plan code May occur a maximum of 8 times. | <RatePlanCandidates> <RatePlanCandidate> RatePlanType=”10” RatePlanCode=”AMX” ID=”987654321” /> |

| /CID | 1-16 1-32 | 20 |  | Corporate ID input by agency (manual input) Worldspan maximum length 20 bytes for membership ID See OTA code table for ProfileType values (ProfileType “1” = Customer) | <AvailRequestSegments> <AvailRequestSegment> < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”CID” MembershipID=”1234567”/> |
| --- | --- | --- | --- | --- | --- |
| /FRT | 1-16 1-32 | 13 |  | Airline Frequent traveler ID Worldspan maximum length 13 bytes for membership ID | <AvailRequestSegments> <AvailRequestSegment> < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”FRT” MembershipID=”1234567890123”/> |
| /FRG | 1-16 1-32 | 17 |  | Hotel Frequent Guest ID Worldspan maximum length 17 bytes for membership ID | <AvailRequestSegments> <AvailRequestSegment> < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”FRG” MembershipID=”1234567890123”/> </Customer> </Profile> </ProfileInfo> |
| /ITN | 1-32 | 13 |  | Inclusive Tour Number Worldspan maximum length 13 bytes | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate InvBlockCode= ”IT78265432109”/> |
| /BT1 | OTA_Code Type Variable | 2 |  | Number of beds and bedding type See code table for BedType code values “5” = Queen Number of beds = Configuration value | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate BedTypeCode=”5” Configuration=”2”> |

### Worldspan Bedding Type Codes:

### Add equiv OTA CODES here

| AP-APARTMENT | VL-VILLA | 2F-2 FULL BEDS |
| --- | --- | --- |
| A1-APARTMENT FOR 1 | V1-VILLA FOR 1 | 2K-2 KING BEDS |
| A2-APARTMENT FOR 2 | V2-VILLA FOR 2 | 2Q-2 QUEEN BEDS |
| A3-APARTMENT FOR 3 | V3-VILLA FOR 3 | 2S-SGL With PULLOUT |
| A4-APARTMENT FOR 4 | V4-VILLA FOR 4 | 2T-2 TWIN BEDS |
| A6-APARTMENT FOR 6 | V6-VILLA FOR 6 | 3B-3 BEDROOMS |
| CB-1 ROOM CABIN | V8-VILLA FOR 8 | 3D-3 DOUBLE BEDS |
| C1-1 BEDROOM CABIN | 1B-1 BEDROOM | 3K-3 KING BEDS |
| C2-2 BEDROOM CABIN | 1D-1 DOUBLE BED | 3Q-3 QUEEN BEDS |
| F1-1 FUTON BED | 1F-1 FULL BED | 3T-3 TWIN BEDS |
| F2-2 FUTON BEDS | 1K-1 KING BED | 4B-4 BEDROOMS |
| JS-JUNIOR SUITE | 1Q-1 QUEEN BED | 4D-4 DOUBLE BEDS |
| JZ-JACUZZI SUITE | 1R-1 ROUND BED | 4K-4 KING BEDS |
| RH-RUN OF HOUSE | 1S-1 SINGLE ROOM | 4Q-4 QUEEN BEDS |
| SJ-LARGE SUITE | 1T-1 TWIN BED | 4T-4 TWIN BEDS |
| ST-STUDIO | 1W-1 WATER BED | 5D-5 DOUBLE BEDS |
| SU-SUITE | 2B-2 BEDROOMS | 5Q-5 QUEEN BEDS |
| S1-1 BEDROOM SUITE | 2D-2 DOUBLE BEDS | 5T-5 TWIN BEDS |
| S2-2 BEDROOM SUITE |  | 6D-6 DOUBLE BEDS |
| S3-3 BEDROOM SUITE |  | 8D-8 DOUBLE BEDS |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /BT2 | Variable | 2 |  | Number of beds and bedding type See OTA code table for BedType code values Note: if two bed types, specified in second occurrence of RoomStayCandidate with no other attributes. | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate BedTypeCode=”6” Configuration=”1”/> |
| /RML | If present, the OTA code will be translated into the WSP 2-byte alpha code | 2 |  | Room location RoomViewCode=”12” Pool view OTA code equivalent to the WSP code 15 = BF-BEACH FRONT 2 = BV-BAY VIEW 24 = CS-COUNTRYSIDE 3 = CV-CITY VIEW 4 = CY-COURTYARD VIEW 16 = GD-GARDEN VIEW 5 = GV-GOLF VIEW 10 = MV-MOUNTAIN VIEW 14 = OF-OCEAN FRONT 11 = OV-OCEAN VIEW 12 = PS-POOLSIDE 12 = PV-POOL VIEW 23 = ST-STRIP VIEW 25 = SV-SEA VIEW | <AvailRequestSegments> <AvailRequestSegment> <RoomStayCandidates> <RoomStayCandidate RoomViewCode=“12”/> |
| /CUR | AlphaLength3 | 3 |  | Currency Code (only sent with Max Rate field) Worldspan fixed length 3 char | <AvailRequestSegments> <AvailRequestSegment> <RateRange CurrencyCode=”USD”/> |
| /MXR | Money decimal value | 7 |  | Maximum rate Worldspan maximum length 7 bytes | <AvailRequestSegments> <AvailRequestSegment> <RateRange MaxRate=”100.00”/> |
| /EMA | Boolean | 0 |  | Exact match indicator Worldspan fixed length 0 char | <OTA_HotelAvailReq ExactMatchOnly=”false”/> |
| /BSM | 1-32 1-32 | 8 |  | IATA number manually input by agent Worldspan fixed length of 8 bytes Type “5” = Travel Agency See OTA Code Table for UniqueID/Type values | <POS> <Source> <RequestorID Type=”5” Instance=”BSM” Id=”12345678”/> </Source> |
| /MOR | 1-32 | 20 |  | More Rates Indicator (for secondary availability Worldspan maximum length 20 bytes | <AvailRequestSegment MoreDataEchoToken=”12345”> |
| /BSA | 1-32 1-32 | 8 | X | IATA number from agent AAA Worldspan fixed length of 8 bytes Type “5” = Travel Agency See OTA Code Table for UnqiueID/Type values | <POS> <Source> <RequestorID Type=”5” Instance=”BSA” Id=”76543210” /> </Source> |
| /BSC | 1-16 | 3 | X | Pseudo city of agent AAA Worldspan fixed length 3 char | <POS> <Source PseudoCityCode=”XYZ”/> |
| /BSI | 1-16 | 2 | X | Agent initials/sine Worldspan fixed length 2 bytes | <POS> <Source AgentSine=”GS”/> |
| /COU | 2 | 2 |  | Country code of AAA Worldspan fixed length 2 char Refer to ISO3166 country code list | <POS> <Source ISOCountry=”US”/> |
|  |  | 1 | X | EOM character c’+’ (ASCIIx’2B’) Note required for internal Worldspan format only |  |

### OTA XML Availability Request Format:

<?xml version="1.0" encoding="UTF-8"?>

<OTA_HotelAvailRQ xmlns="http://www.opentravel.org/OTA/2005/05" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.opentravel.org/OTA/2005/05 OTA_HotelAvailRQ.xsd" Version="1.0" EchoToken="00006#1P#42251#AB345#AV" Target="Production" ExactMatchOnly="false">

<POS>

<Source AgentSine="GS" PseudoCityCode="XYZ" ISOCountry="US">

<RequestorID Type="5" Instance="BSA" ID="99123456"/>

</Source>

<Source>

<RequestorID Type="5" Instance="BSM" ID="12345675"/>

</Source>

</POS>

<AvailRequestSegments>

<AvailRequestSegment MoreDataEchoToken="12345">

<StayDateRange Start="2006-09-18" End="2006-09-23"/>

<RateRange CurrencyCode="USD" />

<RatePlanCandidates>

<RatePlanCandidate RatePlanType="4"/>

<RatePlanCandidate RatePlanType="12"/>

<RatePlanCandidate RatePlanType="14"/>

</RatePlanCandidates>

<Profiles>

<ProfileInfo>

<Profile ProfileType="1">

<Customer>

<CustLoyalty ProgramID="FRT" MembershipID="DL12345"/>

<CustLoyalty ProgramID="FRG" MembershipID="67890"/>

</Customer>

</Profile>

</ProfileInfo>

</Profiles>

<RoomStayCandidates>

<RoomStayCandidate Quantity="1">

<GuestCounts IsPerRoom="1">

<GuestCount Count="2"/>

</GuestCounts>

</RoomStayCandidate>

</RoomStayCandidates>

<HotelSearchCriteria>

<Criterion>

<HotelRef ChainCode="ZZ" HotelCode="12345">

</Criterion>

</HotelSearchCriteria>

<TPA_Extensions>

<RequestType>AV</RequestType>

</TPA_Extensions>

</AvailRequestSegment>

</AvailRequestSegments>

</OTA_HotelAvailRQ>

### Worldspan Availability Request Slash Data Examples:

Symbolic:       (Session Number)(Partition Code) (Agent LNIATA)(Sequence Number)

(Processing Indicator)(Requested Actions)(Hotel Chain Code)

(Hotel City)(Property ID) (Check-in Date)(Check-out Date)

(Number of Persons)(Number of Rooms)

{(Rate Plan Code)} {(Corporate ID)}

{(Plan Code 1-8)} {(Appended Corporate ID 1-8)}

{(Airline Frequent Traveler ID)} {(Hotel Frequent Guest ID)}

{(Inclusive Tour Number)} {(Bedding Type 1)}

{(Bedding Type 2)} {(Room Location)}

{(Currency Code)}

{(Maximum Room Rate)} {(Exact Match Indicator)}

{(Manually Appended IATA Number)}

{(More Rates Indicator)}

(AAA IATA Number)

(AAA City Code)(AAA Agent Initials) {(AAA Country Code)} "+"

Literal:             (NNNNNN)("/COM"XXX )("/LNI"XXXXXX)("/SQN"XXXXX)

("/SYS"A)("/ACT"XX("/CHN"XXX )("/CTY"AAA)("/PID"XXXXX)

("/CKI"NNAAA)("/CKO"NNAAA)("/NPR"N {N})

("/NRM"N) {("/LVL"A..A})} {("/CID"X..X)}

{("/PC1"XXX)} {("/CD1"X..X)}

{("/PC2"XXX)} {("/CD2"X..X)}

{("/PC3"XXX)} {("/CD3"X..X)}

{("/PC4"XXX)} {("/CD4"X..X)}

{("/PC5"XXX)} {("/CD5"X..X)}

{("/PC6"XXX)} {("/CD6"X..X)}

{("/PC7"XXX)} {("/CD7"X..X)}

{("/PC8"XXX)} {("/CD8"X..X)}

{("/FRT"X..X)} {("/FRG"X..X)}

{("/ITN"X..X)}  {("/BT1" {N} A)} {("/BT2" {N} A)}

{("/RML"AA)}

{("/CUR"AA {A} )}{("/MXR"N..N)}

{("/EMA")}  {“/BSM”X..X)} {("/MOR"X..X)}

("/BSA"NNNNNNNN)

("/BSC"XXX)("/BSI"XX) {("/COU"XX)} "+"

Example:        000003/COM1P  /LNI74251C/SQNAB345/SYSS/ACTAV

/CHNZZ /CTYMCI/PID00487/CKI21JUN/CKO25JUN

/NPR2/NRM1/LVLP/CID9012374

/PC1IBM/CD1188231/PC2GEE/CD2882147

/PC3WSP/CD3002813/PC4XYZ/PC5ABC/FRT1234ABC

/FRGABC123/ITNIT5TW1GE03

/BT11Q/BT21K/RMLPS

/CURUSD/MXR75/EMA/BSM12345675/MORIA00012

/BSA99123456/BSCT4S/BSISG/COUUS+

## II. AVAILABILITY RESPONSE (from Associate to Worldspan):

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
|  | These field IDs are part of EchoToken 1-64 | 6 | X | Session Number (6 numerics) Worldspan fixed length 6 bytes | OTA_HotelAvailRS EchoToken=”000006#1P# 42251C#AB345#AV” |
| /COM |  | 3 | X | Partition identifier(alpha, numeric or alpha/numeric) Worldspan fixed length 3 bytes | OTA_HotelAvailRS EchoToken=”000006#1P# 42251C#AB345#AV” |
| /LNI |  | 6 | X | Agents LNIATA(alpha/numeric) Worldspan fixed length 6 bytes | OTA_HotelAvailRS EchoToken=”000006#1P# 42251C#AB345#AV” |
| /SQN |  | 5 | X | Worldspan sequence number (alpha/numeric) Worldspan fixed length 5 bytes | EchoToken=”000006#1P# 42251C#AB345#AV” |
| /SYS | NMToken | 1 | X | Worldspan processing indicator ’Test’ or ‘Production’ | OTA_HotelAvailRS Target=”Production” |
| /RSP | Part of EchoToken | 6 | X | Response type Worldspan fixed length 6 bytes Success: AVLVER - Property Availability Warning AVLERR- No availability: error number or message See OTA Code Table for ErrorWarningType values See OTA Error Code table for “Code” values | OTA_HotelAvailRS <Success/> <Warning Type=”1” Code=”438” ShortText=”Error text” /> |
| /CHN |  | 3 | X | Hotel Chain Code Worldspan fixed length 3 bytes | <RoomStay> <BasicPropertyInfo ChainCode=”XX”> |
| /PID |  | 5 | X | Property Code Worldspan maximum length 5 bytes | <RoomStay> <BasicPropertyInfo HotelCode=”103”> |
| /CKI | 25 | 5 | X | Check-in date YYYY-MM-DD Note: While OTA accepts 25 characters in this field the 10 byte, format Is YYYY-MM-DD. | <RoomStay> <TimeSpan Start=”2003-06-16” /> |
| /CKO | 25 | 5 | X | Check-out date YYYY-MM-DD Note: While OTA accepts 25 characters in this field the 10 byte, format Is YYYY-MM-DD. | <RoomStay> <TimeSpan End=”2003-06-18”/> |
| /NPR | 2 | 1 | X | Number of persons Worldspan fixed length 1 byte | <RoomStay> <GuestCounts IsPerRoom=”1”> <GuestCount Count=”2” /> |
| /TOC |  | 2 |  | Total occupants in room / accommodation Worldspan maximum length 2 bytes | No logical mapping |
| /NCH |  | 2 |  | Number of children in room / accommodation Worldspan maximum length 2 bytes | No logical mapping |
| /MKA |  | 45 |  | Marketing Text Worldspan maximum length 45 bytes See OTA code table for “InfoType” values InfoType“3” = Marketing | <RoomStay> <BasicPropertyInfo> <VendorMessages> <VendorMessage InfoType=”3”> <SubSection> <Paragraph> <Text>Welcome to Hotel Source </Text> </Paragraph> </Subsection> </VendorMessage> </VendorMessages> </BasicPropertyInfo> |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /CUR | Alpha Length 3 | 3 | X | Currency code/type Worldspan maximum length 3 char | <RoomStay> <RoomRates> <RoomRate > <Rates> <Rate> <Base CurrencyCode=”USD”> |
| /BKC | 1-16 | 10 | X | Booking code Worldspan maximum length 10 bytes | <RoomStay> <RoomRates> <RoomRate RoomTypeCode=”1234567890”> AND <RoomStay> <RoomTypes> <RoomType RoomTypeCode=”1234567890”> |
| /CID | 1-32 | 20 |  | Corporate ID Worldspan maximum length 20 bytes | < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”CID” MembershipID= ”1234567890123”/> |
| /LVL |  | 1 |  | Standard Rate Plan Worldspan maximum length 1 byte (see Note below for single character standard rate plans) | <RoomStay> <RoomRates> <RoomRate RatePlanType="4"> |
| /SPC | 1-16 | 10 |  | SecuRate or Negotiated rate plan code Worldspan maximum length 10 bytes The /PC1- /PC8 will all be represented by one field /SPC in the Hotel Availability response. It is not necessary to define them separately on the response since there will be one plan code returned per Booking Code. | <RoomStay> <RoomRates> <RoomRate RatePlanCode="AAA"> |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /FRT | 1-32 | 22 |  | Airline frequent traveler ID Worldspan maximum length 22 bytes | < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”FRT” MembershipID= ”1234567890123”/> |
| /FRG | 1-32 | 17 |  | Hotel frequent guest ID Worldspan maximum length 17 bytes | < Profiles> <ProfileInfo> <Profile ProfileType=”1”> <Customer> <CustLoyalty ProgramID=”FRG” MembershipID= ”12345678901234567”/> |
| /ITN | 1-32 | 13 |  | Inclusive tour number Worldspan maximum length 13 bytes | <RoomStay> <RoomTypes> <RoomType InvBlockCode= ”IT78265432109”/> </RoomType> |

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /RTE |  | 10 | X | Room rate amount Worldspan maximum length 10 bytes Rates must be consistent between Source Availability and Integrated Availability with Rate Range. Each “Rate” element may have only one type of rate amount. A “Rate” element may contain a “Per night before tax”, a “Total before tax”, or a “Total after tax” rate. Type Money of CurrencyCodeGroup | Per night rate before tax <RoomStay> <RoomRates> <RoomRate RoomTypeCode=”1234567890”> <Rates> <Rate> <Base AmountBeforeTax =”105.00”/> --or-- Total rate before tax <RoomStay> <RoomRates> <RoomRate RoomTypeCode=”1234567890”> <Rates> <Rate> <Total AmountBeforeTax=”659.00”/> --or-- Total rate after tax <RoomStay> <RoomRates> <RoomRate RoomTypeCode=”1234567890”> <Rates> <Rate> <Total AmountAfterTax=”682.00”/> |
| /IND | String | 4 | X | Rate indicators A total of (4) of the following will be displayed to the user: “G” = Guarantee required * “D” = Deposit required * * both cannot appear for one rate. Rate includes taxes and surcharges (T) ChangeDuringStay (C) Breakfast included in rate (B) Limited availability (L) Multiple Nights (M) Rate on request status (N) Rate exclusive to Hotel Source (E) | <RoomStay> <RoomTypes> <RoomType ReqdGuaranteeType= ”G”> <RoomStay> <RoomRates> <RoomRate> <Rates> <Rate> <RateDescription> <Text>ChangeDuringStay</Text> <Text>MultipleNights</Text> </RateDescription> |

Ask diane what is the correct text

| Field ID | XML Field Length | Worldspan Specification | Worldspan Mandatory Field | Description | OTA Elements/Attributes |
| --- | --- | --- | --- | --- | --- |
| /CXP |  | 3 | X | Cancellation Policy Code nnH or nH = Hours nnD or nD = Days nnP or nP = PM nnA or nA = AM 99Z = SEE RATE RULES Time should be 24-hour clock Time unit; Hour = number of hours prior to arrival by which the reservation must be cancelled to avoid penalties. Day = number of days prior to arrival by which the reservation must be cancelled. Should this be 99Z or 999 for OTA? 99Z indicates to the user that the cancellation policy is too complex to be identified by a code and they should refer to rate rules. If the first line of room description exceeds 43 characters, and the 44th character is not a blank, to prevent splitting a word Worldspan will backup to the first blank character. This character might be blank or a non character such as a dash (-). The hotel associate should populate either "AbsoluteDeadline" or the combination of "OffsetTimeUnit" and "OffsetUnitMultiplier", but not both. This is consistent with the OTA_HotelAvailRS schema: the annotation for the AbsoluteDeadline element states "...Either this or the offset attributes may be used". | <RoomStays> <RoomStay> <RoomRates> <RoomRate > <Rates> <Rate> <CancelPolicies> <CancelPenalty> For 6PM <Deadline AbsoluteDeadline=”18:00”/> For 10AM <Deadline AbsoluteDeadline=”10:00”/> For Days <Deadline OffsetTimeUnit=”Day” OffsetUnitMultiplier=”1”/> For Hours <Deadline OffsetTimeUnit=”Hour” OffsetUnitMultiplier=”48”/> For “99Z” <Deadline OffsetUnitMultiplier=”999”/> |
| /RMD |  |  |  | Room/rate description text (primary) Worldspan maximum length 43 bytes Needs to be the same information that is returned in the /RMD in Rate Rule response. | <RoomTypes> <RoomType> <RoomDescription> <Text>Room Rate Description Text</Text> </RoomDescription> |

DOES THIS ROW GO WITH THE ONE ON THE NEXT PG

|  |  | 47 |  | Additional room/rate description text Worldspan maximum length 47 bytes Note: Type “1” – Rate Description See code table for AdditionalDetailType values | <RoomType> <AdditionalDetails> <AdditionalDetail Type="1” Code="RD2"> <DetailDescription> <Text>Additional Room Rate Description text</Text> </DetailDescription> </AdditionalDetail> |
| --- | --- | --- | --- | --- | --- |
| /MOR | 1-128 | 20 |  | More Rates Indicator Worldspan maximum length 20 bytes The data returned by the hotel associate in this field should be meaningful to them in identifying where to begin in the next block of data. This value may be sent in the subsequent availability request to see the additional rates. | <RoomStays MoreIndicator=”12345”/> |
| /ERN |  | 18 |  | Error/Warning number-maximum error numbers: 6 - each error number must be 3 characters (alpha/numeric) (3x6=18) See OTA Code Table for “Type” values See OTA Error Code table (will be mapped to Worldspan internal numbers) | <Warnings > <Warning Type=”1” Code=”438”> <Warning Type=”1” Code=”441”> |
| /ERT |  | 384 |  | Error/Warning text | <Warnings> <Warning ShortText=”Error text” Status=”Error”> |
| /AVL |  | 384 |  | Alternate Inn display text -maximum text length: 6 lines of 64 characters each (6x64-384)- total number of lines from /ERN, /ERT, and /AVL combined should not exceed 6 lines excess will be truncated. Note: Type “14” – Miscellaneous Information See code table for AdditionalDetailType values Carriage control must be added to /AVL format for each line | <RoomType> <AdditionalDetails> <AdditionalDetail Type=”14” Code=”AVL”> <DetailDescription> <Text>Alt Property Line 1</Text/> <Text>Alt Property Line 2</Text/> <Text>Alt Property Line 3</Text/> <Text>Alt Property Line 4</Text/> <Text>Alt Property Line 5</Text/> <Text>Alt Property Line 6</Text/> </DetailDescription> </AdditionalDetail> |
|  | 1 |  | X | EOM character c’+’ (ASCII x ‘2B’) Note required for internal Worldspan format only |  |

Note:

- If the /CUR (CurrencyCode) field contains a currency code which is a decimal currency, the rates must have a decimal

position indicated by a period ( . )  Worldspan supports 0 or 2 decimal places.

- The following special characters will be accepted by Worldspan within freeform text fields: asterisk (*), dollar sign ($),

dash (-), period (.) and a space.

### OTA XML Availability Response Format:

<?xml version="1.0" encoding="UTF-8"?>

<!--Hotel Avail Response Only 1 RoomType/Rate Returned -->

<OTA_HotelAvailRS xmlns="http://www.opentravel.org/OTA/2003/05" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.opentravel.org/OTA/2003/05 OTA_HotelAvailRS.xsd" Version="1.0" EchoToken="00006#1P#42251#AB345AV" Target="Production">

<Success/>

<POS>

<Source AgentSine="GS" PseudoCityCode="XYZ" ISOCountry="US">

<RequestorID Type="5" Instance="BSA" ID="99123456"/>

</Source>

<Source>

<RequestorID Type="5" Instance="BSM" ID="12345675"/>

</Source>

</POS>

<Profiles>

<ProfileInfo>

<Profile ProfileType="1">

<Customer>

<CustLoyalty ProgramID="FRT" MembershipID=" DL12345"/>

<CustLoyalty ProgramID="FRG" MembershipID="67890"/>

</Customer>

</Profile>

</ProfileInfo>

</Profiles>

<RoomStays >

<RoomStay>

<RoomTypes>

<RoomType RoomTypeCode=" A01MI3" InvBlockCode="IT7865432109"

ReqdGuaranteeType="G">

<RoomDescription>

<Text>PROMOTIONAL</Text>

</RoomDescription>

<AdditionalDetails>

<AdditionalDetail Type="1" Code="RD1">

<DetailDescription>

<Text>1 KING BED</Text>

</DetailDescription>

</AdditionalDetail>

</AdditionalDetails>

</RoomType>

</RoomTypes>

<RoomRates>

<RoomRate RoomTypeCode=" A01MI3">

<Rates>

<Rate>

<Total AmountBeforeTax="294..00" CurrencyCode="USD"/>

<CancelPolicies>

<CancelPenalty>

<Deadline AbsoluteDeadline="18:00"/>

</CancelPenalty>

</CancelPolicies>

</Rate>

</Rates>

</RoomRate>

</RoomRates>

<GuestCounts>

<GuestCount Count="2"/>

</GuestCounts>

<TimeSpan Start="2006-09-18" End="2006-09-21"/>

<BasicPropertyInfo ChainCode="ZZ" HotelCode="12345">

<VendorMessages>

<VendorMessage InfoType="3">

<SubSection>

<Paragraph>

<Text> MKAPLACE NS IN SI FIELD FOR NONSMOKING </Text>

</Paragraph>

</SubSection>

</VendorMessage>

</VendorMessages>

</BasicPropertyInfo>

<AlternateInfo/>

</RoomStay>

</RoomStays>

</OTA_HotelAvailRS>

### OTA XML Availability Response Format: (Error Response - AVLERR)

(refer to OTA Error Code Table values)

<?xml version="1.0" encoding="UTF-8"?>

<!-- Hotel Avail Response Error - Requested Rate Not Available-->

<OTA_HotelAvailRS xmlns="http://www.opentravel.org/OTA/2003/05" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.opentravel.org/OTA/2003/05 OTA_HotelAvailRS.xsd" Version="1.0"

EchoToken="00006#1P#42251#AB345AV" Target="Production">

<Success/>

<Warnings>

<Warning Type="1" Code="438" ShortText="Requested Rate Not Available" Status="Error"/>

</Warnings>

<RoomStays>

<RoomStay>

<BasicPropertyInfo ChainCode="XX"/>

<AlternateInfo/>

</RoomStay>

</RoomStays>

</OTA_HotelAvailRS>

OTA XML Availability Response Format: (Error Response with Alternate Inn Display)

(refer to  OTA Error Code Table values)

<?xml version="1.0" encoding="UTF-8"?>

<!--Hotel Avail Response Error - Alternate Properties returned-->

<OTA_HotelAvailRS xmlns="http://www.opentravel.org/OTA/2003/05" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:schemaLocation="http://www.opentravel.org/OTA/2003/05 OTA_HotelAvailRS.xsd" Version="1.0"

EchoToken="00006#1P#42251#AB345AV" Target="Production">

<Success/>

<Warnings>

<Warning Type="1" Code="376" ShortText="Hotel full check alternate" Status="Error"/>

</Warnings>

<RoomStays >

<RoomStay>

<RoomTypes>

<RoomType>

<AdditionalDetails>

<AdditionalDetail Type="14" Code="AVL">

<DetailDescription>

<Text>122: XX –  ATLANTA INN BUCKHEAD </Text>

<Text> PROPERTY IS 0 KM EAST OF 134</Text>

<Text>838: XX  –  MIDTOWN ATLANTA </Text>

<Text> PROPERTY IS 6 MI SOUTH OF 134</Text>

<Text>1114: XX – W ATLANTA </Text>

<Text> PROPERTY IS 7 MI NORTH OF 134</Text>

</DetailDescription>

</AdditionalDetail>

</AdditionalDetails>

</RoomType>

</RoomTypes>

<BasicPropertyInfo ChainCode="XX"/>

<AlternateInfo/>

</RoomStay>

</RoomStays>

</OTA_HotelAvailRS>

#### Example Hotel Source Availability Responses from Hotel Associate to Worldspan:

Example 1

Three character field IDs are in bold until they repeat again

|  | 1 2 3 4 5 6 1234567890123456789012345678901234567890123456789012345678901234 |
| --- | --- |
| 01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 | >COM1P /LNI021213/SQNA0651/SYSS/RSPAVLVER/CHNHH /PID23561/CKI23O CT/CKO30OCT/NPR2/MKAPLACE NS IN SI FIELD FOR NONSMOKING/CURHKD/B KCA00A33/CIDN0002690/RTE2750.00/CXP2D/INDG/RMDAMEX EMEA/RD11 KIN G BED DELUXE MOUNTAIN VIEW/BKCA0CA33/CIDN0002690/RTE2750.00/CXP2 D/INDG/RMDAMEX EMEA/RD12 TWIN BEDS DELUXE MOUNTAIN VIEW/BKCA0NA3 3/CIDN0002690/RTE3250.00/CXP2D/INDG/RMDAMEX EMEA/RD12 TWIN BEDS DELUXE OCEAN VIEW/BKCA0MA33/CIDN0002690/RTE3250.00/CXP2D/INDG/RM DAMEX EMEA/RD11 KING BED DELUXE OCEAN VIEW/BKCA01A33/CIDN0002690 /RTE3350.00/CXP2D/INDG/RMDAMEX EMEA/RD11 KING BED EXECUTIVE ROOM /BKCA0DA33/CIDN0002690/RTE3350.00/CXP2D/INDG/RMDAMEX EMEA/RD12 T WIN BEDS EXECUTIVE ROOM/BKCA0OA33/CIDN0002690/RTE3850.00/CXP2D/I NDG/RMDAMEX EMEA/RD11 KING EXEC FLR OCEAN VIEW/BKCA0PA33/CIDN000 2690/RTE3850.00/CXP2D/INDG/RMDAMEX EMEA/RD12 TWIN EXEC FLR OCEAN VIEW/BKCA09A33/CIDN0002690/RTE5200.00/CXP2D/INDG/RMDAMEX EMEA/R D11 BEDROOM SUITE WITH PARLOR/BKCA0QA33/CIDN0002690/RTE5700.00/) |

Example 2

|  | 1 2 3 4 5 6 1234567890123456789012345678901234567890123456789012345678901234 |
| --- | --- |
| 01 02 03 04 05 06 07 08 09 10 11 12 13 14 15 | >COM1P /LNI021213/SQNA0651/SYSS/RSPAVLVER/CHNHH /PID23561/CKI23O CT/CKO30OCT/NPR2/MKAPLACE NS IN SI FIELD FOR NONSMOKING/CURHKD/B KCA00A33/CIDN0002690/RTE2750.00/CXP2D/INDG/RMDAMEX EMEA/RD11 KIN G BED DELUXE MOUNTAIN VIEW/BKCA0CA33/SPCAMX/CIDN0002690 /RTE2750.00/LVLN/CXP2D/INDG/RMDAMEX EMEA/RD12 TWIN BEDS DELUXE MOUNTAIN VIEW/BKCA0NA3/SPCAMX/CIDN0002690/RTE3250.00/LVLN/CXP2D /INDG/RMDAMEX EMEA/RD12 TWIN BEDS DELUXE OCEAN VIEW/BKCA0MA33/ SPCAMX/CIDN0002690/RTE3250.00/LVLN/CXP2D/INDG/RM DAMEX EMEA/RD11 KING BED DELUXE OCEAN VIEW/BKCA01A33/SPCIBM/CIDN0002689 /RTE3350.00/LVLN/CXP2D/INDG/RMDAMEX EMEA/RD11 KING BED EXECUTIVE ROOM /BKCA0DA33/SPCIBM/CIDN0002689/RTE3350.00/LVLN/CXP2D/INDG /RMDAMEX EMEA/RD12 T WIN BEDS EXECUTIVE ROOM/BKCA0OA33/SPCIBM/ CIDN0002689/RTE3850.00/LVLN/CXP2D/I NDG/RMDAMEX EMEA/ RD11 KING EXEC FLR OCEAN VIEW/BKCA0PA33/SPCSBC/CIDN0002611/ RTE3850.00/LVLN/CXP2D/INDG/RMDAMEX EMEA/RD12 TWIN EXEC FLR )> |

Error response:

123456/COMNW /LNI520912/SQNF543E/SYSS/RSPAVLERR/CHNZZ /ERN175

/ERTNO RATES FOUND FOR RATE PLAN REQUESTED - TRY ANOTHER+

Alternate property availability (original hotel requested is not available):

123456/COM1P /LNIFEB290/SQN5CDCF/SYSS/RSPAVLERR/CHNZZ /ERNP01/AVL123:

ZZ - AIRPORT HOTEL

PROPERTY IS 0 MI EAST OF 123

345: ZZ – NORTHTOWN

PROPERTY IS 0 MI EAST OF 123

678: ZZ - SOUTHTOWN

PROPERTY IS 0 MI EAST OF 123

# Footnotes

Net Rate plan of ‘X’ has been submitted to OTA Hotel Work Group Dec. 2005.  Pending.

The rate plan ‘X’ cannot be combined with any other (new Dec. 2005).  The rate plan code of ‘X’ was submitted to the OTA Hotel Working Group in Dec. 2005 for addition to the OTA codes.

# Text boxes

If receive ‘12’ send PV