NOTICE:

This device complies with Part 15 of the FCC Rules. Operation shall be subject to the following two conditions: This device may not cause harmful interface, and This device must accept any interface received, including interface that may cause undesirable operation.

This equipment has been tested and complied with the limits for a Class a digital device, pursuant to Part 15 of the FCC Rules. These limits are designed to provide a reasonable protection against harmful interface when the equipment is operated under a commercial environment. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instruction manual, may cause harmful interface to radio communications. Operation of this equipment in a residential area is likely to cause harmful interface in which case the user will be required to correct the interface at his own expenses.

Note: All brands and trademarks shall belong to their respective owner.

Note: Specification is subject to changes without notice.

Using the ArgoxScan 8110/8150/8250/8310/8312

The ArgoxScan can automatically scan barcode at a distance. Simply aim and pull the trigger. Code scanning is performed along the center of the light bar emitted from the reading window. This bar must cover the entire code.

Successful scanning shall be obtained by tilting the scanner with respect to the barcode to avoid direct reflections that impair the reading performance, especially for 2D barcode.

## Recommended Steps

When the required settings have been configured, all settings are stored in non- volatile memory of scanner after reading EXIT Label. Recommended steps are as follows.

- Set right host interface for your scanner.

(The scanner is in factory default shown as bold label)

- Set interface to optimize protocol of scanner with your host in interface section.

- Set system control of scanner, such as specific adjustments double confirm, power saving, indicator and scanning mode which you prefer usage in system control section.

- Set code options of scanner for your usage in code option section. You must make sure to enable the symbology first, then Min./Max. code length, code ID checksum and truncate digits are also converted.

- Set string format of the scanner, such as preamble, postamble Prefix, suffix, code ID and code name transmission for your application in string format section.

Note: If still not work properly. Please contact your dealer for further information.

## CONTENTS

| Chapter 1 Introduction |  |
| --- | --- |
| Introduction…………………………..………………. | 1 |
| Default Setting ………………………………………. | 2 |
| ArgoxScan8110 specification …………………….. | 4 |
| ArgoxScan8150/8250/8310/8312 specification ….. | 7 |
| Programming the ArgoxScan…………………….. | 10 |
| Chapter 2 Parameter Setting |  |
| Interface……………………………………………….… | 12 |
| Interface Selection ………………………………….. | 12 |
| Keyboard wedge ……………………………………. | 13 |
| RS-232 …………………………………………….…. | 18 |
| Wand Emulation …………………………….………. | 21 |
| Pin Assignments ……………………………………. | 24 |
| System Control………………………………………. | 28 |
| Scan …………………………………………………. | 28 |
| Indication …………………………..………………… | 34 |
| Code Option…………………………………….……… | 36 |
| UPCA ……………………………………..…………. | 36 |
| UPCE ………………………………………………… | 42 |
| EAN-13 ………………………………………………. | 46 |
| EAN-8 ………………………………………………… | 50 |
| Code 39 ……………………………………………… | 54 |
| Interleaved 2 of 5 …………………………………… | 58 |
| Industrial 2 of 5 ……………………………………… | 60 |
| Matrix 2 of 5 Eur …………………………………… | 62 |
| Codabar ……………………………………………… | 64 |
| Code-128 …………………………………………… | 67 |
| Code-93 ……………………………………………… | 71 |
| Code-11 ………………………………………….…… | 74 |
| MSI/Plessey …………………………………………. | 76 |
| UK/Plessey ………………………………………….. | 78 |
| Telepen ………………………………………………. | 80 |
| Standard 2 of 5 ……………………………………… | 82 |
| China Post …………………………………………… | 84 |
| Italian pharmacode ………………………………… | 86 |
| Code 16K …………………………………..………… | 88 |
| PDF-417 ……………………………………………… | 90 |
| EAN UCC Composite……………………………….. | 92 |
| RSS-14 ………………………………………………. | 94 |
| RSS-Limited…………………………………..…… | 96 |
| RSS-Expanded…………………………………..….. | 98 |
| Micro-PDF…………………………………..……….. | 100 |
| String Format…………………………………………… | 102 |
| String Setting / Transmission (Prefix/Suffix)………………………………………… | 102 |
| String Setting / Transmission (Preamble/Postamble)……………………………… | 104 |
| String Setting / Transmission (Insert Group Characters)………………………….. | 106 |
| String Setting / Transmission (Others)…….………………………………………… | 110 |
| Appendix………………………………………………… | 112 |
| Test Chart ……………………………………………. | 112 |
| ASCII Code Table …………………………………… | 115 |
| Parameter setting List ………………………………. | 116 |