IMSAI

8K BASIC

Version 1.4

Copyright 1977 IMSAI Manufacturing Corporation

14860 Wicks Boulevard

San Leandro, California 94577

Made in the U. S. A.

All rights reserved worldwide.

81-0000036 Rev. B

BASIC 8A Rev. 0

Loading

IMSAI 8K BASIC

Version 1.4

I. Loading

IMSAI 8K BASIC is available on three media: paper tape,

Tarbell format cassette, and EPROM.

The paper tape and cassette versions require a minimum of 12K

of RAM installed at contiguous addresses from zero up.  More

RAM will permit longer BASIC programs and/or more variables.

A. Loading the Paper Tape Version

Use the IMSAI Paper Tape Loader, as supplied with your

IMSAI 8080 to load the paper tape.  Follow the

instructions for loading paper tapes in the User

Manual (Chapter 12, System Software).  For the

convenience of those who do not have the IMSAI Paper

Tape Loader, a copy of its documentation is included

with each order for BASIC on paper tape.

If your memory has WRITE PROTECT switches, turn the

first 8K bytes off.

B. Loading the Cassette Version

Use the IMSAI Tape Cassette Bootstrap Loader (PGM-5A)

to load the cassette.  Follow the instructions

supplied with the loader.  A copy of the loader

documentation is included with the cassette as an aid

those who do not have the IMSAI loader.

Alternately, IMSAI's Tape Cassette Operating System

(PGM-2A) may be used to load the BASIC cassette.  In

this case, start execution with the TCOS command

EXEC 0.

If your memory has WRITE PROTECT switches, turn the

first 8K bytes off.

C. Installing the EPROM Version in Your System

Insert the 32 chips in two IMSAI PROM 4 boards, taking

care that each chip has pin 1 up and is in the correct

socket for its address.

Jumper the boards for address 0 and 1000 hex and install

them in the machine.

Install RAM starting at address 2000 hex.  4K of RAM

is adequate for many programs; 8K BASIC will make use

of as much RAM as is installed at contiguous

addresses starting at 2000 hex.

1						BASIC 8A Rev. 0

Starting, Programs

II. Starting BASIC

Hit STOP, RESET, RUN (if the loader started BASIC, skip this

step.)

BASIC should type "READY".

Hit the CR key and then type NEW CR.  This step is essential

when BASIC is first started.

III. Restarting BASIC

If the system gets hung up and will not respond to control-C,

try restarting BASIC.

Do this by hitting STOP, RESET, RUN in the front panel.

Your program should still be in memory and may be LISTed,

modified, or RUN.

IV. Entering a Program from the Keyboard

Type the command NEW to delete the previous program.

Enter the program one line at a time, typing a CR after each

line.

Each statement must be numbered, but they need not be typed

in order.  The program will be listed or executed in line

number order.  It is suggested that successive line numbers

differ by 10 or more to permit inserting lines later.

A line may be deleted by typing its line number followed by

a CR.

A line may be replaced by typing the same line number

followed by the updated statement and CR.

A line may be inserted by typing a new, unique line number,

followed by the statement and CR.

A line may be retyped if a mistake is noticed before the CR

is typed by typing control-U.

The last character may be deleted by typing the RUBOUT key.

A back slash, the deleted character,  and another back

slash will echo.  On a CRT terminal, you may delete the

previous character by typing control-H which will erase the

previous character and back the cursor up one position.

Now type the correct character and continue.

V. Entering a Program from Paper Tape

Type the command NEW to delete the previous program.

2

BASIC 8A Rev. 0

Listing

Mount the paper tape in the Teletype reader starting

anywhere in the leader.

Type the command TAPE.

Manually start the reader, if necessary.

If the tape was not punched by this BASIC, after it has

been read, stop the reader and type KEY CR.

VI. Listing the Program

Type the command LIST CR.

To list a single statement, type LIST line number CR.

To list a portion of the program, type LIST line number,

line number CR.

To interrupt a LIST in progress, type control-C.

VII. Punching the Program on Paper Tape

Type SAVE, but do not type the CR.

Turn on the teletype punch.

Hits CR.

The program will be punched and listed.

Turn off the punch.

VIII. Running the Program

Type the command RUN.

The program will run to completion until an error is

encountered or until a stop statement is executed.

The program may be terminated by typing control-C.

INPUT statements will prompt with a question mark.  Type

the value and a CR.  Multiple values may be input separated

by commas.

IX. Error Messages

BASIC error messages are of the form: XX ERR @ 9999 where XX

3

BASIC 8A Rev. 0

Error Messages

is the error code and 9999 is the line number.  (Immediate

commands print no line number.)

The following errors terminate program execution:

Code	Meaning

DA	Out of data.  A READ statement

tried to read another DATA

value and there were no more

DATA statements.

NX	NEXT with no matching FOR or

more than 8 nested FORs.

UL	Unidentified line number in

IF...THEN, GOTO, or

GOSUB statement.

RT	RETURN encountered and no

GOSUB in effect.

OF	Fatal overflow: division by zero,

attempt to take log of a number

less than or equal to zero, or

square root of a negative number

(other overflow errors are

non-fatal; see below).

SN	Syntax error: unidentified

statement or incorrectly formed

statement; BASIC can't

understand what you're saying.

ST	Execution stack (internal)

error. Either:

1) a NEW command was not given

after power-up;

2) too few or too many argu-

ments for a function; or

3) some syntax errors give

the "ST" error code.

The following errors are non-fatal; i.e., a message is

printed and program execution continues.

Code	Meaning

UN	Underflow: number whose absolute

value is less than 2.71050 E-20

and greater than zero.

4

BASIC 8A Rev. 0

Debugging

OV	Overflow: number whose absolute

value is greater than 5.76461 E18

(slightly higher values may be

reached using addition or

subtraction).

X. Debugging

After correction, the program may be restarted with the

command GOTO 9999 where 9999 is the line number given

in the message, or with the CON command.

The program may be stopped by typing control-C.

Variables may be inspected with the PRINT (or ?) command.

Variables may be modified with the LET or INPUT commands.

Output may be suppressed without stopping the program by

typing control-O.  Another control-O will turn printout

on again.

XI. References

This manual is not intended to be an introduction to the

BASIC language.  Users with no familiarity with BASIC are

referred to the following books, all available from IMSAI:

My Computer Likes Me When I Speak BASIC, by Bob Albrecht

An introduction to BASIC for those with no

previous computer experience.

BASIC-Plus Manual, Digital Equipment Corp.

User manual for a minicomputer BASIC; 8K BASIC is

similar to languages described in first few

sections.

What To Do After You Hit Return, People's Computer Company

A book of game programs written in BASIC.

XII. IMSAI BASIC Language

Notation: In the following two sections

CAPITAL letters represent words that are used

verbatim.

Lower case words are representative, for instance,

"variable" means "X", "Y1", "Q9$" or any legal

BASIC variable name.

[square brackets] enclose optional items.

"..." means the variable or expression may be

repeated any number of times.

5

BASIC 8A Rev. 0

Statements

Don't forget the commas (or semi-colons) between

the repetitions.

Statements:

[LET] variable=expression

DIM variable (dimensions)

for numeric variables only; should appear before

variable is used.

PRINT expression, expression ...

prints values at 14 column tab stops

PRINT expression; expression ...

prints without space between

PRINT

alone prints carriage return

All PRINTouts end with a carriage return unless

the statement contained a comma or semi-colon

after the last expression.

?

Same as PRINT

INPUT variable, variable ...

prompts with "?" and accepts typed-in numbers

or strings.  If "text" is used in place of a

variable, it is typed out.

REM any text

!

Same as REM

IF expression relop expression THEN line number or

statement

"relop" can be <, =, >, <> (not equal), >=, <=.

FOR expression=expression TO expression [STEP expression]

NEXT variable

GOTO line number

GOSUB line number

INPUT LINE string variable

Accepts typed-in text terminated by a carriage

return.  Any quotes, commas or spaces in the

text are transmitted.

RETURN

6

BASIC 8A Rev. 0

Statements, Expressions

ON expression GOTO line number, line number ...

ON expression GOSUB line number, line number ...

DATA value, value ...

RESTORE

READ variable, variable ...

DEF FN variable (variable(s))=expression

CHANGE array name=string variable

CHANGE string variable=array name

STOP

stops execution; program can be restarted

with CON

END

optional; stops execution, program cannot

be restarted with CON

CALL expression

calls user's machine language routine at

address given by expression

POKE address, value

stores 8-bit value into memory; e.g., for

transmitting data to machine-language

routing.

OUT port, value

outputs value to port for accessing

non-standard I/O devices

RANDOMIZE

Expressions

Variables consist of a letter or a letter and

a digit, followed by a dollar sign for

string-valued variables.

Number range is 2.7105E-20 to 5.7646E18.

Numeric operators available are +, -, *, / and

^ (raise to a power).  On some keyboards ^ is ^.

Strings may be 0 to 238 characters long.

String constants (literal texts) may be

enclosed in single or double quotes.

The "+" operator concatenates strings.

7

BASIC 8A Rev. 0

Functions

Functions Available:

All arguments may be expression. Those

ending in "$" are string-valued.

ABS(x)	    Absolute value

SQR(x)	    Square root

INT(x)	    Largest integer <= x

SGN(x)	    Sign of x: -1, 0 or 1

RND[(x)]	    Random number between

0 and x.  If (x) is

omitted, range is 0 and 1.

SIN(x)

COS(x)

TAN(x)

ATN(x)

LN(x)	    Natural logarithm

LOG(x)	    Base 10 logarithm

EXP(x)

PEEK(address)    Contents of memory location

PI		    3.14159

LEN(string)	    Length

INSTR(x,string1,string2)

Position of string2 in string1

starting at position x; 0 if

not found

ASCII(string)    ASCII value of character

CHR$(x)	    String consisting of character

with ASCII value x

STRING$(x,y)	    String of x characters with

ASCII value y

NUM$(x)	    Converts number to string of

digits

VAL(string)	    Numeric value of string (gives

CV error if not numeric)

SPACE$(x)	    String of x spaces

LEFT$(string,n)  Characters 1 through n of

string

RIGHT$(string,n) Characters n through end

of string

MID$(string,m,n) n characters of string

starting at character m.

POS(x)	    Carriage position.  First

column is 0, x is ignored.

TAB(x)	    Use only with PRINT.  Moves

carriage to column x.

INP(port)	    Input from I/O port

Multiple statements on one line are allowed if

separated by colons.

8

BASIC 8A Rev. 0

Immediate Commands

XIII. Immediate Commands

The following may be typed without a line number for

immediate execution.

LIST

RUN

XEQ	Like RUN but does not delete data

GOTO

NEW

NEW*	Deletes program without deleting

data, for chaining

TAPE

SAVE

KEY

FREE

CON	Continue from STOP, control-C or

after correcting an error

IF	Typed without the THEN clause to

test variables.  For example:

IF A=B CR. If you get,

UL ERR @ LINE then the relation is

true.  Otherwise, it's false.

In addition, almost all BASIC program statements, if typed

without a line number, will be executed immediately.

XIV. Chaining

Some applications involve a program too large to fit the

available memory.  Techniques described here permit

"chaining" multiple programs while transmitting variable

values from one to the next.

Load and RUN the first program in the normal

manner.

Use "NEW*" rather than "NEW" to delete the program

without deleting its data.

Enter or load the next program in the normal manner.

Use XEQ rather than RUN to start the program without

clearing the data are.

Repeat the preceding three steps for each additional

program.

9

BASIC 8A Rev. 0

Compatibility, Known Problems

XV. Compatibility

A. With BASIC-Plus

Line numbers range from 1 to 9999 only.

Subscripts not allowed on string variables.

Number range: 2.7105-E20 to 5.7646E18.

Only the statements, operators, and functions

listed above area available.

B. With Previous Release 1.3

Log function gives Base 10 Logarithm rather than

natural logarithm.

New function LN gives natural logarithm.

PRINT ... TAB(X) ...: If X is less than the column

position goes to a new line.  Old version continued

at current column.

XVI. Known Problems

"FRE" returns a number that includes storage actually in use

for variables.

If program size exceeds memory available, BASIC bombs out.

If data (variable values) exceed size of memory not used by

program, program and possibly interpreter is destroyed.

If program jumps (with a GOTO) out of a FOR loop before the

loop has completed then later executes the same FOR

statement, BASIC gets confused.

There is no provision for reserving memory for machine

language routines other than by addressing an additional

board at non-contiguous address.

Strings over about 238 characters cause a variety of

problems including interfering with the current FOR loop

and destroying the BASIC interpreter.

10