`

NURIT 2159

Electronic Cash Register

With Integrated Card Processor

User Manual

January 2006

Table of Contents

Introduction	1

An Overview of the NURIT 2159	1

The Terminal Keyboard	2

User Operations	4

Loading the Register Data Records	4

Opening the Register	5

Example of Register Opened Report	6

Opening the Cash Drawer	7

Example of Open Cash Draw Reports	9

Closing the Register	10

Examples of Register Closed Reports	12

Batch Report	12

Batch Report Explanations	13

Z Reports	15

Changing Cashiers	17

Completing a Sales Transaction	18

Methods for Entering Transaction Information	18

Entering Item – Via PLU	19

Entering Multiples of Item – Via PLU	19

Entering Item – Via PLU Hot Keys	20

Entering Multiples of Item – Via PLU Hot Keys	20

Entering Item – Via Scanner	21

Entering Multiples of Item – Via Scanner	21

Entering Item – Via Department	22

Entering Multiples of Item – Via Department	22

Entering Items – Via Department Hot Keys	23

Entering Multiples of Item – Via Department Hot Keys	23

Examples of Single and Multiple Entries	24

Voiding Single Items	25

Example of Voided Items	25

Printing Receipt Copies	26

Sales	27

Cash Sale	27

Example of Cash Receipt	28

Credit Card Sale	29

Example of Credit Card Receipt	30

Debit Card Sale	31

Example of Debit Card Receipt	32

Check Sale	33

Example of Check Receipt	34

EBT Card Sale	35

Example of EBT Receipt	36

Coupons	37

Example of Receipt with Coupons	38

Gift Cards	39

Example of Gift Card Receipt	41

Table of Contents, Continued

Discounts	42

Item Discount	42

Sub Total Discount	43

Examples of Item and Sub Total Discounts	44

Additional Transaction Types	45

General Refund	45

Examples of Refund Receipt	46

Void	47

Example of Void Receipt	48

Verify	49

Forced	50

Gift Card	51

Gift Card Purchase	51

Gift Card Refund	53

Gift Card Issuance	54

Gift Card Add Value	55

Gift Card Void	56

Gift Card Balance	57

Gift Card Batch Issue	58

Gift Card Post Authorization	59

Gift Card Transfer	60

Loyalty Card	61

Loyalty Card Void	61

Loyalty Card Balance	62

Loyalty Card Post Authorization	63

Loyalty Card Transfer	64

Loyalty Card Add Points	65

Phone Card	66

Phone Card Purchase	66

Phone Card TopUp	68

Phone Card Bill Payment	70

Menu Functions	72

Reports	72

Setting the X/Z Default Reports	74

Print X Report	75

Settings Report	76

Non Resettable Report	77

Register Reports	78

Periodical Report	79

Cumulative Report	80

Journal Report	81

Display Transactions	82

ECR Options	83

Delete Journal	83

Delete PLU File	84

Setting the Halo	85

PLU Print	86

Table of Contents, Continued

Department Print	87

Receipt Print	88

Change Discount	90

Force Client	91

Set Communication Time	92

Set Communication Parameters	93

Allow Unknown PLU	95

Edit Journal Number	96

Merchant Options	97

Operation Mode	97

Debit Double Receipt	98

Invoice Mode	99

Security Menu	100

Menu / Batch	100

Open / Close Register	101

Open Drawer	102

Void / General Refund	103

Change Discount	104

ECR Reports	105

Edit Menu	106

Edit Header / Trailer	106

Edit Hot Keys	108

Creating New PLUs	109

Editing Existing PLUs	111

Creating New Departments	113

Editing Existing Departments	114

Creating New Cashiers	116

Editing Existing Cashiers	117

Tax Menu	118

Set Tax %	118

Tax Name	119

System Options	120

Set Time/Date	120

Site ID	121

Reset the Database	122

BarCode Functions	123

Print BarCodes	123

POS Functions	124

POS Communications	125

Line Parameters	125

Maximum Retries	125

Dial Type	126

Dialing Prefix	127

Phone Number Display	128

Break Mode	129

Table of Contents, Continued

POS Reports	130

Report Types	130

Default Report	131

Current Report	132

History Reports	134

Performance Report	136

Report Setup – Printing Visa/MC Options	137

Communication Utilities	138

Batch to Host	138

Transaction Upload	139

PLU Download	140

Department Download	141

Cashier Download	142

Client Download	143

Auto Load	144

Employee Report	145

NURIT 2159 QUICK REFERENCE GUIDE	146

Appendix A	147

| Important! | Appendix A of this manual is essential and therefore should be read carefully and thoroughly prior to use of this product. (See page 147) |
| --- | --- |

## Introduction

The NURIT 2159 is a fully functional electronic cash register (ECR) plus completely integrated Point-Of-Sale (POS) / Electronic Draft Capture (EDC) terminal designed mainly for small to mid-range retail merchants. The culmination of many years of cash register and POS terminal technology is found in this sophisticated and user-friendly product. You will find that the NURIT 2159 will handle all of your business needs with its ability to accept all popular means of payment such as cash, credit, debit and private label cards, to name a few. In addition, the NURIT 2159 comes standard with easily accessible ports for additional peripherals such as an external PIN pad, barcode reader, check reader, etc.

## An Overview of the NURIT 2159

| Information | This section will provide you with a basic understanding of the operations and functionality of the NURIT 2159. This will include a keyboard overview and a basic explanation of common terms that you will find throughout this manual. The NURIT 2159 has thirty-six (36) keys (11 alphanumeric, 17 specialty and 8 multifunction hot keys). |
| --- | --- |

#### The Terminal Keyboard

| Key | Function |
| --- | --- |
| [OPEN/CLOSE REGISTER] Open/Close Register | Used to open and close the cash register. |
| [COMM/UTILITY] Communications Utility | Used to access the PC/Backend Communication. |
| [OPEN DRAWER] Open Drawer | Used to electronically open a cash drawer when it is connected to the NURIT 2159 smart cash register. It is also used to record Paid In and Paid Out cash transactions. |
| [MENU/ESC] Menu Escape | Used to enter and exit the terminal’s menus. It is also used to answer no to terminal questions. |
| [TRANS TYPE] Transaction Type | Used to access the terminal’s General Refund transaction. |
| [TIME CLOCK] Time Clock | Used to access the employee time clock function if it is available in the current terminal application. |
| [REVIEW] Review | Used to review transactions in the current open journal or batch. |
| [SPECIAL] Special | Used to temporarily close the cash register without batching or closing the open journal. This key is also used to reopen the register when it is set to Temp. Closed. Use this key to switch cashiers. |
| [1-8] Hot Keys | Used to select the payment option (credit, cash, debit, etc.) when processing a transaction. The keys can also be set for department and PLU hot keys. |
| [0], [1] – [9], and [00] Number Keys | Used to enter all numerical values. Also, all the number keys, except for [00], are used in conjunction with the [ALPHA/COPY] key to enter alphabet text and various symbols. |
| [ALPHA/COPY] | Used in conjunction with the number keys to enter alphabet text and various symbols. It is also used to print transaction receipt copies. |
| [CANCEL/VOID] | Used to cancel an operation and to void a transaction or item while the transaction is being performed. |

Continued on next page.

The Terminal Keyboard, Continued

| Key | Function |
| --- | --- |
| [PLU/(] | Used when entering a PLU (Price Look Up) during a transaction and to scroll through menu options. |
| [DEPT/(] | Used when entering a department during a transaction and to scroll through menu options. |
| [ENTER] | Used to select a menu item, answer the yes to onscreen questions, and to progress a transaction through to the Total Payment option. |
| [PAPER FEED/(] | Used to backspace when entering data or in conjunction with the [CTRL] key to advance the paper roll one line at a time. |
| [DSCNT/ (] | Used when entering a discount during a transaction and to scroll through menu options. |
| [QTY/(] | Used when entering a quantity during a transaction and to scroll through menu options. |
| [CTRL] | Used in conjunction with other keyboard keys to perform secondary functions. Hold down and tap the PAPER FEED key to advance the register tape. |

## User Operations

#### Loading the Register Data Records

| Information | After the register has been loaded with the Application and Host Processor information, the parameters or data records (i.e. Cashiers, Departments, PLUs, Customers and such) that were created using the NURIT Store Manager must be downloaded into the NURIT 2159. The register cannot be opened until this information has been loaded. |
| --- | --- |

Note

After the Application and Host Processor information has been downloaded, the register will prompt to change the Site ID. The Site ID should be the same as the number on the Manager Card.

| Step | Action | Display |
| --- | --- | --- |
|  | If the number displayed is the same as the Manager Card number, press [MENU/ESC]. Note: Press [ENTER] and follow prompts to change. |  |
|  | Press [COMM UTILITY] |  |
|  | Press [7]. |  |
|  | A processing message is briefly displayed. |  |
|  | The register will contact the NURIT Store database and download the information. |  |
|  | When the download is complete, the register will return to the ECR CLOSED display. |  |
|  | Stop |

#### Opening the Register

| Information | Opening the register refers to the process of opening a new Journal and activating the register to process transactions. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press the [OPEN/CLOSE REGISTER] button from the ECR CLOSED screen prompt. |  |
|  | Swipe the Manager Card. OR Press [MENU/ESC]; enter the daily password and press [ENTER]. |  |
|  | The following message is briefly displayed. |  |
|  | If this is the first time the register has been opened after the download, enter the new journal number then press [ENTER] |  |
|  | Enter the Opening Bank amount then press [ENTER]. The Opening Bank is the amount of cash that is in the cash drawer at the beginning of the day or shift. |  |
|  | Note: If you choose to use the default Opening Bank, just press [ENTER]. The Opening Bank from the previous day or shift is the default dollar amount. If this is a newly programmed register the default amount will be $0.00. If an Opening Bank amount is not entered when the unit is in Stand Alone Mode, the bank will be $0.00. |
|  | Type in the Discount amount (IF ANY) then press [ENTER]. Press [ENTER] with no amount for zero discount. Note: The previously entered discount amount will display. Press [ENTER] to accept. |  |

Continued on next page.

Opening the Register, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the Cashier ID and press [ENTER]. |  |
|  | The current system date and time will appear. |  |
|  | The register is now ready to process transactions. |
|  | Stop. |

#### Example of Register Opened Report

#### Opening the Cash Drawer

| Information | Once the Register is open, the Cash Drawer can be opened to: Exchange bills for change. Pay money in. Pay money out. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [OPEN DRAWER]. |  |
|  | Swipe the Manager Card. OR Press [MENU/ESC]; enter the daily password and press [ENTER]. |  |
|  | If you want to: Action Open the draw with no change to drawer balance. Press [1] to Open Drawer Pay money into drawer. Press [2] for Paid In Pay money out of drawer. Press [3] for Paid Out |  |
|  | If “1” was pressed, the cash drawer will open. Note: See Step #5 for Paid In. Note: See Step #10 For Paid Out. |  |
|  | Enter the Paid In amount then press [ENTER]. |  |
|  | Enter the reason for the money being Paid In then press [ENTER] OR Press [ENTER] to bypass. |  |
|  | To enter the reason, press the number that has the desired letter displayed on the key then press the [ALPHA/COPY] key to change the number to the letter. I.E.: for the letter “M” press the [6] key then press [ALPHA/COPY] once. |

Continued on next page.

Opening the Cash Drawer, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Swipe the Manager Card. OR Press [MENU/ESC]; enter the daily password and press [ENTER]. |  |
|  | A short Paid In report will print and the Cash Drawer will open. |  |
|  | Note: Continued from Step #3 Enter the Paid Out amount then press [ENTER]. |  |
|  | Enter the reason for the money being Paid In then press [ENTER] OR Press [ENTER] to bypass. Note: See Step #7. |  |
|  | Swipe the Manager Card. OR Press [MENU/ESC]; enter the daily password and press [ENTER]. |  |
|  | A short Paid Out report will print and the Cash Drawer will open. |  |
|  | Stop. |

#### Example of Open Cash Draw Reports

#### Closing the Register

| Information | Closing the register refers to closing of the current Journal. At the end of each day or shift, it is necessary to close the register. The current EDC Batches can also be closed at this time. If they are turned on, the following reports will be printed when the Register is closed: ▪ Journal ▪ Cumulative ▪ Department ▪ Cashier ▪ PLU ▪ Batch (when closing batches) |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [OPEN/CLOSE REGISTER] from the “Ready” prompt. |  |
|  | Swipe the Manager Card. OR Press [MENU/ESC]; enter the daily password and press [ENTER]. |  |
|  | Press [ENTER] to Close Batch OR Press [MENU/ESC] for NO. |  |
|  | Press [ENTER] to close the batch for all hosts. OR Scroll down and press [ENTER] to select specific host. Note: A Batch Report for the selected EDC types will print. |  |
|  | Press [ENTER] |  |
|  | Press [ENTER] to continue. Note: The terminal is going to print out the active reports; this message is to prompt you to ensure there is enough paper to print the reports. |  |

Continued on next page.

Closing the Register, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | The terminal is going to ask if you would like to print this report again. Press [ENTER] for Yes or [MENU/ESC] for No. |  |
|  | The register will briefly display a number of communication messages and print a Bridge Report. Note: Does not apply to Stand Alone Mode. |  |
|  | The terminal will now return to the ECR CLOSED screen prompt. |  |
|  | Stop. |

#### Examples of Register Closed Reports

Note

Reports must be turned on in the Reports Menu. See page 74.

Unless the Default Report Type is set to journal, the full credit card account number will not be printed. To print a Journal report or to set the default type to journal, see pages 130 to 133.

##### Batch Report

Note

You should close the batch for every EDC type that processed transactions for that day

##### Batch Report Explanations

| Credit | The transactions types displayed in the report are: SL – Sale; amount will be added to the EDC and overall total. VE – Verify; amount will not be included in the totals. TK – Forced (Ticket Only); amount will be included in the totals. RT – Return (General Refund); amount will be deducted from the totals. |
| --- | --- |

| Debit | The transactions types displayed in the report are: SL – Sale; amount will be added to the EDC and overall total. RT – Return (General Refund); amount will be deducted from the totals. |
| --- | --- |

| Check | For Check processing, the only type of transaction that is supported is Sale. SL – Sale; amount will be added to the EDC and overall total. |
| --- | --- |

| Gift/Loyalty Card | The transactions types displayed in the report are: RE – Redemption; amount will be added to the EDC and overall total. IS – Issuance; amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. AV – Add Value; amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. VD – Void (Gift & Loyalty); zero amount PA – Post Authorization (Gift & Loyalty); amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. BI – Batch Issue; amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. BA – Balance (Gift & Loyalty); zero amount AP – Add Points (Loyalty); amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. |
| --- | --- |

Continued on next page.

Batch Report Explanations, Continued

| Phone Card | The transactions types displayed in the report are: PN – PIN Sale; amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. CR – Card TopUp (Credit); amount added to the Phone Account. Amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. RE – Card TopUp (Refund); amount deducted from the Phone Account. Zero amount. BP – Bill Payment; amount will not be included in the totals. Amount paid at time of purchase will be listed under correct payment type. |
| --- | --- |

##### Z Reports

Z Reports, Continued

#### Changing Cashiers

| Information | The cashier ID that was entered when the register was opened can be changed without closing and re-opening the register. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Make sure the register is in the ready state. |  |
|  | Press [SPECIAL] |  |
|  | Press [SPECIAL] |  |
|  | Enter the new Cashier ID then press [ENTER]. |  |
|  | Stop |

## Completing a Sales Transaction

| Information | The NURIT 2159 is capable of performing sales transactions using a choice of payment options, including cash and all electronic forms of payment (if available to the merchant). The basic instructions in this section assume that all PLUs, Departments, and Taxes (the 2159 can be programmed with up to three separate tax amounts), have already been programmed. Also, all transactions assume that the register is open. Note: The cash register will not operate without either Departments or PLU’s having been programmed. |
| --- | --- |

### Methods for Entering Transaction Information

| Information | Use any of the five methods listed below to enter transaction information. |
| --- | --- |

| Method | Description |
| --- | --- |
| By PLU | Type in the Unique PLU code and press [PLU]. |
| By PLU Hot keys | Press the appropriate PLU Hot key. [1] – [8] |
| By Scanner | Scan the barcode on the item. |
| By Department | Input the dollar amount of the sale and press the [DEPT] key. Type in the desired department number. |
| By Department Hot Keys | Type in the sale amount and press the required department hot key [1-8] |

#### Entering Item – Via PLU

| Information | Once the 2159 Cash Register has been programmed with PLU codes (Price Look-Up codes) you can enter a transaction by manually entering the PLU number. Use the following Step/Action table for assistance. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Type in the last unique digits of the PLU number of the item. Note: If the PLU begins with zeros you can type it in starting with the first non-zero digit. |  |
|  | Press [PLU] Note: The Exc 123 means that the item is exempt from taxes #1, #2 and #3. |  |
|  | Repeat steps 1 & 2 for all items. |
|  | Stop. |

#### Entering Multiples of Item – Via PLU

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the quantity of the item purchased then press [QTY]. |  |
|  | Type in the last unique digits of the PLU number of the item. Note: If the PLU begins with zeros you can type it in starting with the first non-zero digit. |  |
|  | Press [PLU] |  |
|  | Stop. |

#### Entering Item – Via PLU Hot Keys

| Information | You can utilize the PLU Hot keys [1] through [8] only after the Hot Keys have been programmed. Use the following Step/Action table for assistance. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press the Hot Key that is assigned to the item you are entering. Note: The Exc 23 means that the item is exempt from taxes #2 and #3 but not from tax #1. |  |
|  | Stop. |

#### Entering Multiples of Item – Via PLU Hot Keys

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the quantity of the item purchased then press [QTY]. |  |
|  | Press the Hot Key that is assigned to the item you are entering. |  |
|  | Stop. |

#### Entering Item – Via Scanner

| Information | The scanner functionality is available only after you have programmed the PLU’s. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Find the Bar Code on the item. |
|  | Press the button on the under side of the scanner to activate the reader. |
|  | With the button still pressed slide the scanner over the bar code. Note: The unit will beep indicating it scanned the code. |  |
|  | Stop. |

#### Entering Multiples of Item – Via Scanner

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the quantity of the item purchased then press [QTY]. |  |
|  | Find the Bar Code on the item. |
|  | Press the button on the under side of the scanner to activate the reader. |
|  | With the button still pressed slide the scanner over the bar code. Note: The unit will beep indicating it scanned the code. |  |
|  | Stop. |

#### Entering Item – Via Department

| Information | Items can be entered by department after you have successfully programmed the departments into the unit. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Using the number keys input the dollar amount of the item. Note: It is not necessary to enter the decimal. |  |
|  | Press [DEPT]. |  |
|  | Input the corresponding department # Press [ENTER] |  |
|  | Stop. |

#### Entering Multiples of Item – Via Department

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the quantity of the item purchased then press [QTY]. |  |
|  | Using the number keys input the dollar amount of the transaction. Note: It is not necessary to use the decimal. |  |
|  | Press [DEPT]. |  |
|  | Input the corresponding department # Press [ENTER] |  |
|  | Stop. |

#### Entering Items – Via Department Hot Keys

| Information | Items can be entered via the department hot keys after you have successfully programmed the department hot keys into the unit. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Using the number keys input the dollar amount of the transaction. Note: It is not necessary to use the decimal. |  |
|  | Press the Department Hot Key that corresponds with the item you are entering. |  |
|  | Stop. |

#### Entering Multiples of Item – Via Department Hot Keys

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the quantity of the item purchased then press [QTY]. |  |
|  | Using the number keys input the dollar amount of the transaction. Note: It is not necessary to use the decimal. |  |
|  | Press [DEPT]. |  |
|  | Input the corresponding department # Press [ENTER] |  |
|  | Stop. |

#### Examples of Single and Multiple Entries

Note

Items entered by PLU information are displayed the same on the receipt regardless of method of entry.

Items entered by Department are displayed the same on the receipt regardless of method of entry but are displayed differently than items entered by PLU.

#### Voiding Single Items

| Information | If an item is entered in a transaction incorrectly, the item can be voided from the transaction. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the items using any of the previously explained methods. |  |
|  | Press [CANCEL/VOID] |  |
|  | Enter the item to be voided using any of the previously explained methods. |  |
|  | Stop. |

#### Example of Voided Items

#### Printing Receipt Copies

| Information | A copy of the Last Receipt (Gift Receipt with no amounts or Regular) or Any Receipt from the current journal can be printed. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | From the ready screen press the [ALPHA/COPY] key. |  |
|  | Swipe the Manager Card. |  |
|  | For Last Receipt Press [1] For Action Gift Receipt Press [1] Regular receipt Press [2] |  |
|  | For Any Receipt Press [2] Enter the daily password then press [ENTER] Enter the transaction number then press [ENTER] |  |
|  | Stop. |

### Sales

#### Cash Sale

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the items using one of the methods from pages ??. |
|  | After all items have been input press [ENTER]. Note: The dollar amount will represent the current total for this transaction prior to adding taxes or deducting discounts. You can still add items or deduct discounts from this prompt. |  |
|  | Press [ENTER] Note: The dollar amount will represent the current total for this transaction including taxes that were added and any deductions that were made. You can no longer add new items or deduct discounts from this point. |  |
|  | Enter the cash amount tendered. |  |
|  | Press [CASH] If Then No Change is required A receipt will print and the display will go back to the READY prompt. Change is required A receipt will print out and the terminal will display the amount of change that should be given. Press [ENTER] to return to the READY prompt. |
|  | Stop. |

#### Example of Cash Receipt

#### Credit Card Sale

| Step | Action | Display |
| --- | --- | --- |
|  | After all items have been input press [ENTER]. Note: The dollar amount will represent the current total for this transaction prior to adding taxes or deducting discounts. You can still add items or deduct discounts at this prompt. |  |
|  | Press [ENTER] Note: The dollar amount will represent the current total for this transaction including taxes that were added and any deductions that were made. You can no longer add new items or deduct discounts after pressing ENTER. |  |
|  | Press [CREDIT] |  |
|  | Swipe the customer’s credit card with the magnetic stripe down and facing right. (You can input the account # and expiration date manually if necessary by using the number keys.) Note: The unit will beep to indicate the card has been read. |  |
|  | Press [ENTER]. The register will print a receipt. Note: The actual authorization code will be displayed. |  |
|  | Press any key. The terminal will now print a second receipt for the customer. |  |
|  | Stop. |

#### Example of Credit Card Receipt

#### Debit Card Sale

| Step | Action | Display |
| --- | --- | --- |
|  | After all items have been input press [ENTER]. Note: The dollar amount will represent the current total for this transaction prior to adding taxes or deducting discounts. You can still add items or deduct discounts at this prompt. |  |
|  | Press [ENTER] Note: The dollar amount will represent the current total for this transaction including taxes that were added and any deductions that were made. You can no longer add new items or deduct discounts after pressing ENTER. |  |
|  | Press [DEBIT] |  |
|  | Swipe the customer’s debit card. |  |
|  | Enter the Cash Back amount then press [ENTER] or just press [ENTER] to bypass. |  |
|  | Instruct the customer to type their PIN number and press [ENTER] on the external PIN pad. |  |
|  | If the PIN number is valid the terminal will now dial the host. If the debit card is approved, the terminal will print a receipt. By default, the terminal will only print one (1) debit receipt. |
|  | Stop. |

#### Example of Debit Card Receipt

#### Check Sale

| Step | Action | Display |
| --- | --- | --- |
|  | After all items have been input press [ENTER]. Note: The dollar amount will represent the current total for this transaction prior to adding taxes or deducting discounts. You can still add items or deduct discounts at this prompt. |  |
|  | Press [ENTER] Note: The dollar amount will represent the current total for this transaction including taxes that were added and any deductions that were made. You can no longer add new items or deduct discounts after pressing ENTER. |  |
|  | Press [CHECK] |  |
|  | Enter the amount on the check then press [ENTER]. |  |
|  | Manually enter the MICR number then press [ENTER] or swipe the check through a check reader. Note: This screen will differ slightly depending on your current check host. |  |
|  | If MICR was manually entered, enter the Check Number then press [ENTER]. |  |
|  | Enter the Cash Back amount then press [ENTER] or just press [ENTER] to bypass. |  |
|  | Depending on the check host, the terminal will either dial and process at this point or the screen will prompt you for additional host specific information. Type in the requested information and press [ENTER]. |
|  | The terminal will now dial and then print a receipt with an either APPROVAL or DENIAL response code. |
|  | Stop. |

#### Example of Check Receipt

#### EBT Card Sale

| Step | Action | Display |
| --- | --- | --- |
|  | After all items have been input press [ENTER]. Note: The dollar amount will represent the current total for this transaction prior to adding taxes or deducting discounts. You can still add items or deduct discounts at this prompt. |  |
|  | Press [ENTER] Note: The dollar amount will represent the current total for this transaction including taxes that were added and any deductions that were made. You can no longer add new items or deduct discounts after pressing ENTER. |  |
|  | Press [OTHER PAYMENT] to scroll to the EBT option. |  |
|  | Press [ENTER]. |  |
|  | Swipe the customer’s EBT card. |  |
|  | If Then Food Stamp Press [1] Input the sale amount then press [ENTER] Have the customer input the PIN number on the external PIN Pad then press [ENTER] Cash Benefit Press [2] Input the desired Cash Back Amount Have the customer input the PIN number on the external PIN Pad then press [ENTER] |  |
|  | Stop. |

#### Example of EBT Receipt

#### Coupons

| Information | This function will allow you to deduct the coupon amount from the item’s price. You can also use coupon as a method of payment for the entire purchase should the action you are performing require you to do so. (I.e.: Store Credit) |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Process the sale to the Choose Tender prompt. |  |
|  | Input the amount of the coupon. |  |
|  | Press [OTHER PAYMENT] to the coupon option then press [ENTER]. |  |
|  | Enter the coupon number then press [ENTER] Note: If more than 1 coupon is being entered repeat steps 2 – 4 |  |
|  | Complete the sale by selecting a payment method. |
|  | Stop. |

#### Example of Receipt with Coupons

#### Gift Cards

| Information | This function will allow you to deduct the Gift Card amount from the total payment due or use the Gift card to absorb the total amount of the entire purchase should the card value equal or exceed the total payment due. Use the Step/Action table below for assistance. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Process the sale to the Choose Tender prompt. |  |
|  | Press [OTHER PAYMENT] to select the gift card option then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER]. |  |
|  | Press [ENTER]. |  |
|  | Press [ENTER] |  |
|  | Swipe the Gift card. |  |
|  | Press [ENTER] |  |

Continued on next page.

Gift Cards, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | The Host response is briefly displayed. |  |
|  | Press any key to print the receipt. |  |
|  | Press any key to print a second receipt. |  |
|  | Stop. |

#### Example of Gift Card Receipt

### Discounts

#### Item Discount

| Information | Use the following Step/Action table for assistance discounting specific merchandise. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the item that is being discounted. Press [DISCNT] |  |
|  | For Then Discount in % Press [1] Discount in $ Press [2] |  |
|  | Enter the percentage or dollar amount then press [ENTER]. |  |
|  | Complete the sale. Note: The type of discount will be indicated by the first character on the second line. |  |
|  | Stop. |

#### Sub Total Discount

| Information | Use the following Step/Action table for assistance when discounting the overall subtotal of a sale. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Complete the sale to the Sub Total prompt. |  |
|  | For Then Discount in % Press [1] Discount in $ Press [2] |  |
|  | Enter the percentage or dollar amount then press [ENTER]. |  |
|  | Complete the sale. |  |
|  | Stop. |

#### Examples of Item and Sub Total Discounts

### Additional Transaction Types

| Information | ( General Refund ( Void ( Verify ( Forced ( Phone Card ( Gift / Loyalty Card This transaction type is accessed by pressing the [TRANS TYPE] Key. Use the Step/Action tables below for assistance. |
| --- | --- |

#### General Refund

Note

General Refund is supported by Cash, Credit and Debit only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] then press [ENTER]. | The current system date & time will appear |
|  | Follow the instructions for a sale transaction. |
|  | The terminal receipt will print REFUND at the top. |
|  | Stop. |

#### Examples of Refund Receipt

#### Void

Note

Only Cash transactions can be voided. Check, Coupon, Credit, Debit, EBT and Gift Card transactions cannot be voided.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until VOID is displayed. |  |
|  | Press [ENTER] |  |
|  | Enter the transaction number then press [ENTER]. |  |
|  | The register will prompt to Void by Cash. Press [ENTER]. |  |
|  | Stop. |

#### Example of Void Receipt

#### Verify

Note

This function is supported by the Credit EDC only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until VERIFY is. |  |
|  | Press [ENTER]. |  |
|  | Enter the amount of the Verify then press [ENTER]. |  |
|  | Swipe the credit card. |  |
|  | Stop. |

#### Forced

Note

Forced is only for Credit Card transactions where the Authorization Code is already known.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until VERIFY is displayed then press [ENTER]. |  |
|  | Enter the transaction items using any of the methods previously explained. |  |
|  | Proceed to the CHOOSE TENDER screen. |  |
|  | Press [CREDIT] then swipe card or manually enter the account number and expiration date. |  |
|  | Enter the previously obtained authorization code then press [ENTER] |  |
|  | Stop. |

#### Gift Card

| Information | A special department is automatically created for Gift/Loyalty cards, this is Department 97. When the card is purchased, the amount to be assigned to the card is entered as the price. After the transaction is completed and paid for, the register will automatically prompt for the card to be issued. |
| --- | --- |

##### Gift Card Purchase

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the purchased items using any of the methods previously explained. |  |
|  | Enter the dollar amount to be assigned to the Gift/Loyalty card. |  |
|  | Press [DEPT] |  |
|  | Enter [9], [7] then [ENTER]. |  |
|  | Enter the remaining items being purchased |  |
|  | Complete the transaction |  |
|  | The gift card authorization message is briefly displayed. |  |
|  | Enter the Clerk ID then press [ENTER] |  |

Continued on next page.

Gift Card Purchase, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Press [ENTER] |  |
|  | Press [2] |  |
|  | Swipe the newly purchased Gift/Loyalty Card. |  |
|  | Enter the amount to be assigned to the card. |  |
|  | Press [ENTER] |  |
|  | The Host response will be briefly displayed |  |
|  | Press any key to continue. |  |
|  | Stop. |

##### Gift Card Refund

Note

If the Issuance does to complete for any reason, the register automatically starts a process to refund the amount collected to assign to the card.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press any key. |  |
| 2. | Press [ENTER] |  |
| 3. | Enter the amount paid for the gift card. |  |
| 4. | Press [DEPT] |  |
| 5. | Enter [9], [7] then [ENTER]. |  |
| 6. | Complete the transaction using the same payment type as the original transaction. |  |
| 7. | Press any key. |  |
| 8. | Stop |

##### Gift Card Issuance

Note

If the gift card was purchased without using Department #97, the card can be issued using the TRANS TYPE key.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [2] |  |
|  | Swipe the newly purchased card. |  |
|  | Enter the amount to be assigned to the card then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Add Value

Note

The amount being added to the gift card should be processed as a normal Gift/Loyalty Card purchase or with a different PLU/ Department as the merchant wishes.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. OR Process the transaction using Department #97 |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [3] |  |
|  | Swipe the gift card. |  |
|  | Enter the amount to be added to the card balance then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Void

Note

When selecting the VOID in the Gift Card menu you can void any type of process where an Authorization Code was given; i.e. sale using a gift card, issuance, add value or transfer.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [4] |  |
|  | Swipe the gift card or manually enter the account number. |  |
|  | Enter the authorization code of the transaction to be voided then press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Balance

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [5] |  |
|  | Swipe the gift card or manually enter the account number. |  |
|  | The Host response is briefly displayed. A receipt will be printed listing the card balance. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Batch Issue

Note

The Batch Issue function can be used to Issue, for the same amount, a group or batch of cards with consecutive account numbers.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [6] |  |
|  | Swipe the first of the consecutively numbered gift cards. |  |
|  | Enter the amount to be issued to each of the cards then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Swipe the last of the consecutively numbered gift cards. |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Post Authorization

Note

Use the Post Authorization function to enter a transaction for which the authorization code has already been obtained.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [7] |  |
|  | Swipe the gift card or manually enter the account number. |  |
|  | Enter the authorization code then press [ENTER] |  |
|  | Enter the amount then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Gift Card Transfer

Note

This function is used to transfer the balance from one card to another.

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press [8] |  |
|  | Swipe the old/original gift card or manually enter the account number. |  |
|  | Swipe the new card. |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

#### Loyalty Card

| Information | Gift and Loyalty Cards are the same cards with Loyalty Points added to the card as the customer makes purchases. The money spent is added to the card. This money is then converted to loyalty points are then converted again to dollars and added to the Gift total of the card in a Host back-end process. |
| --- | --- |

##### Loyalty Card Void

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [2] |  |
|  | Press [ENTER] |  |
|  | Swipe the gift card or manually enter the account number. |  |
|  | Enter the authorization code then press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Loyalty Card Balance

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [2] |  |
|  | Press [2] |  |
|  | Swipe the loyalty card or manually enter the account number. |  |
|  | The Host response is briefly displayed. A receipt will be printed listing the card balance. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Loyalty Card Post Authorization

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [2] |  |
|  | Press [3] |  |
|  | Swipe the loyalty card or manually enter the account number. |  |
|  | Enter the authorization code then press [ENTER] |  |
|  | Enter the amount then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Loyalty Card Transfer

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [2] |  |
|  | Press [4] |  |
|  | Swipe the old/original loyalty card or manually enter the account number. |  |
|  | Swipe the new card. |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

##### Loyalty Card Add Points

| Step | Action | Display |
| --- | --- | --- |
|  | From the “READY” Prompt press [TRANS TYPE] until GIFT/LOYALTY is displayed then press [ENTER]. |  |
|  | Enter the clerk ID then press [ENTER] |  |
|  | Press [2] |  |
|  | Press [5] |  |
|  | Swipe the loyalty card or manually enter the account number. |  |
|  | Enter the amount of the purchase then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | The Host response is briefly displayed. |  |
|  | Press [ENTER] |  |
|  | Stop. |

#### Phone Card

| Information | A special department is automatically created for Phone cards, this is Department 98. When the card is purchased, the amount to be assigned to the card is entered as the price. After the transaction is completed and paid for, the register will automatically prompt for the card to be issued. Funds can also be added to an existing card/account and consumer bills can be paid if the Payee ID and account number are known. |
| --- | --- |

##### Phone Card Purchase

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the purchased items using any of the methods previously explained. |  |
|  | Enter the dollar amount to be assigned to the Phone card. |  |
|  | Press [DEPT] |  |
|  | Enter [9], [8] then [ENTER]. |  |
|  | Enter the remaining items being purchased |  |
|  | Complete the transaction |  |
|  | The phone card authorization message is briefly displayed. |  |
|  | Enter the Clerk Password then press [ENTER]. |  |

Continued on next page.

Phone Card Purchase, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Press [ENTER] |  |
|  | Enter the Service Provider Code from the supported list supplied by the Host Processor then press [ENTER] |  |
|  | Enter the amount assigned to the account then press [ENTER] |  |
|  | Press any key. |  |
|  | Stop. |

##### Phone Card TopUp

Note

If the customer already has purchased a phone card or obtained an account, funds can be added to the account using the TopUp function.

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the purchased items using any of the methods previously explained. |  |
|  | Enter the dollar amount to be added to the previously purchased Phone card/account. |  |
|  | Press [DEPT] |  |
|  | Enter [9], [8] then [ENTER]. |  |
|  | Enter the remaining items being purchased |  |
|  | Complete the transaction |  |
|  | The phone card authorization message is briefly displayed. |  |
|  | Enter the Clerk Password then press [ENTER]. |  |
|  | Press [2] |  |

Continued on next page.

Phone Card TopUp, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Press [1] to credit/add money to the account. OR Press [2] to refund money from the account. |  |
|  | Swipe the phone card or manually enter the account number then press [ENTER] |  |
|  | Enter the amount added to or refunded from the account then press [ENTER] |  |
|  | Stop. |

##### Phone Card Bill Payment

Note

The Phone Card protocol can also be used to pay bills when the Payee ID and Account Numbers are known.

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the purchased items using any of the methods previously explained. |  |
|  | Enter the dollar amount of the bill being paid. |  |
|  | Press [DEPT] |  |
|  | Enter [9], [8] then [ENTER]. |  |
|  | Enter the remaining items being purchased |  |
|  | Complete the transaction |  |
|  | The phone card authorization message is briefly displayed. |  |
|  | Enter the Clerk Password then press [ENTER]. |  |
|  | Press [3] |  |

Continued on next page.

Phone Card Bill Payment, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Enter the Payee ID then press [ENTER] |  |
|  | Enter the account number then press [ENTER] |  |
|  | Re-enter the account number then press [ENTER] |  |
|  | Enter the dollar amount of the bill being paid then press [ENTER] |  |
|  | Stop. |

## Menu Functions

| Information | This section will focus on the Menu of the NURIT 2159, which is used to program and customize all functions and modes of operation for the terminal. The menu is divided into main menus and sub-menus that can be accessed by pressing the [MENU/ESC] key. |
| --- | --- |

### Reports

Definitions

| Report | Definition | Quick Reference |
| --- | --- | --- |
| Cashier Report | The Cashier report gives the totals summary for each cashier. It shows the quantity of transactions done by each cashier, total amount, and the percentage of total sales. It can be printed as a stand-alone report and included on an X or Z report. The register must be open to print this report. | Menu( 1 ( 5 ( 3 |
| Cumulative Report | The Cumulative Report will give you totals from the first day the register was used. It includes all active EDC types, coupon and total refunds. | Menu( 1 ( 7 |
| Department Report | The Department report gives you the totals of each department for the day. It prints the quantity of items sold in each department, total amount, and percentage of sales. It can be printed as a stand-alone report and included on an X or Z report. The register must be open to print this report. | Menu( 1 ( 5 ( 2 |
| Display Transaction | Will display individual transaction information in the current journal or closed journals. | Menu( 1 ( 9 |
| Journal Report | The Journal report will print out a copy of each transaction for a specific journal. | Menu( 1 ( 8 |
| Periodical Report | This is an hourly report of transaction and amount totals per hour and overall totals. | Menu( 1 ( 6 |

Continued on next page

Definitions, Continued

| Report | Definition | Quick Reference |
| --- | --- | --- |
| PLU Report | This is a daily report of each PLU sold. It will print the number of PLUs sold, and the dollar amount. It can be printed as a stand-alone report and included on an X or Z report. The register must be open to print this report. | Menu( 1 ( 5 ( 1 |
| Non Resettable | The Non Resettable report shows the cumulative dollar amounts for the register from day one. This report includes all sales and refunds sorted by form of payment. It also shows the totals for Tax 1, Tax 2, and Tax 3. This report cannot be reset. | Menu( 1 ( 4 |
| Settings | The Settings Report lists the ECR Application, system HALOs, number of Departments and PLU set up, Hot Key settings, Backend communications and Tax settings. | Menu( 1 ( 3 |
| Time and Attendance Report | This is a daily report of the time and attendance of each cashier. The register must be open to print this report. | Menu( 1 ( 5 ( 4 |
| X Report | The X report is a combination of reports that shows an up to date tally of transaction information within the terminal without closing the register or batching. This report can consist of the: Journal Report, Cumulative Report, Department Report, Cashier Report, and PLU Report. | Menu( 1 ( 2 |
| X/Z Defaults | Activates/Deactivates the various reports that are printed when the register is closed or X Report is selected. | Menu( 1 ( 1 |

| Report Menu Information | The first menu in the NURIT 2159 is the Report Menu. It is divided into (9) nine different sub menus that are used to print and set the parameters for different types of reports. The sub menus are as follows: X/Z Defaults, Print X Report, Settings, Non Resettable, Register Reports, Periodical Report, Cumulative Report, Journal Report and Display Transactions. |
| --- | --- |

#### Setting the X/Z Default Reports

| Information | This option allows you to set the reports that will print on the X and Z reports. The available reports are: Journal Report, Cumulative Report, Department Report, Cashier Report, and PLU Report. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Press the up [DISCNT ] or down [QTY ] arrow keys to toggle between OFF and ON. |  |
|  | Press [ENTER] after making your selection. |  |
|  | Repeat steps 4 & 5 for Cumulative Report, Department Report, Cashier Report, and PLU Report. |  |
|  | Stop. |

#### Print X Report

| Information | The X report is a combination of reports that shows an up to date tally of transaction information within the terminal without closing the register or batching. This report can consist of the: Cumulative Report, Journal Report, Department Report, Cashier Report, and PLU Report. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [ENTER] |  |
|  | Press [2] |  |
|  | Verify that there is enough paper on the paper roll then press [ENTER] |  |
|  | A message is briefly displayed then the report is printed. |  |
|  | Stop. |

#### Settings Report

| Information | The Settings Report lists the ECR Application, Header Information, system HALOs, number of Departments and PLU set up, Hot Key settings, Backend communications and Tax settings. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [ENTER] |  |
|  | Press [3] |  |
|  | Stop. |

#### Non Resettable Report

| Information | The Non Resettable report shows the cumulative dollar amounts for the register from day one. This report includes all sales and refunds sorted by form of payment. It also shows the totals for Tax 1, Tax 2, and Tax 3. This report cannot be reset. |
| --- | --- |

Note

The register must be closed to run this report.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ECR Closed prompt |  |
|  | Press [ENTER] |  |
|  | Press [4] |  |
|  | Stop. |

#### Register Reports

| Information | This menu allows you to print the PLU Report, Department Report, Cashier Report and T&A (Time & Attendance) Report. Each report (except for T&A) shows totals within the current Journal. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [ENTER] |  |
|  | Press [5] |  |
|  | Press [ENTER] |  |
|  | Use the [] and [] keys to scroll through the available reports. Press [ENTER] to print the report. |
|  | Repeat Step 5 for each report of choice. |
|  | Stop. |

#### Periodical Report

| Information | This sub-menu allows you to print a report while the register is open showing amount totals and number of transactions sorted by hour. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [ENTER] |  |
|  | Press [6] |  |
|  | Stop. |

#### Cumulative Report

| Information | This sub-menu allows you to print a cumulative report that shows the activity in the last closed batch and includes the following items: Total Amount, Total Amount Items, Charge Amount, Charge Amount Items, Refund Amount, EDC Amount (sorted by EDC Type), Cash in Drawer, Opening Bank, Drawer Income, Drawer Outcome, Drawer Opened (number of times) and Tax Income. |
| --- | --- |

Note

The register must be closed to run this report.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from ECR CLOSED prompt. |  |
|  | Press [ENTER] |  |
|  | Press [7] |  |
|  | Stop. |

#### Journal Report

| Information | This sub-menu allows you to print a cumulative report that shows the activity in the last closed batch and includes the following items: Total Amount, Total Amount Items, Charge Amount, Charge Amount Items, Refund Amount, EDC Amount (sorted by EDC Type), Cash in Drawer, Opening Bank, Drawer Income, Drawer Outcome, Drawer Opened (number of times) and Tax Income. |
| --- | --- |

Note

The register must be closed to run this report.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from ECR CLOSED prompt. |  |
|  | Press [ENTER] |  |
|  | Press [8] |  |
|  | Stop. |

#### Display Transactions

| Information | This sub-menu allows you to review the properties (Items purchased, Transaction Type, Department, Total w/ Tax, and Payment Type) of a specific transaction within a specific journal. |
| --- | --- |

Note

Only transactions in the current journal are displayed in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [ENTER] |  |
|  | Press [9] |  |
|  | Input Journal # and press [ENTER]. |  |
|  | Input the Transaction # and press [ENTER]. |  |
|  | Press [ENTER] to scroll through transaction details. | Note: The terminal will display the actual transaction # and transaction type. |
|  | Stop. |

### ECR Options

| Information | The second menu in the NURIT 2159 is the ECR Options menu. This menu is divided into (12) twelve sub-menus. |
| --- | --- |

#### Delete Journal

| Information | This sub-menu is used to delete the current journal information. |
| --- | --- |

Note

The Register must be closed for this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ECR CLOSED prompt. |  |
|  | Press [2] |  |
|  | Press [ENTER] |  |
|  | Swipe the Manager Card. |
|  | Stop. |

#### Delete PLU File

| Information | This sub-menu is used to delete the current PLU information. |
| --- | --- |

Note

The Register must be closed for this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ECR CLOSED prompt. |  |
|  | Press [2] |  |
|  | Press [2] |  |
|  | Swipe the Manager Card. |  |
|  | Stop. |

#### Setting the Halo

| Information | This sub-menu allows you to disable or set the transaction HALO (maximum transaction amount). |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [2] |  |
|  | Press [3]. |  |
|  | Enter the maximum transaction amount then press [ENTER] |  |
|  | Stop. |

#### PLU Print

| Information | This sub-menu allows you to print the PLUs currently programmed in the terminal. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
| g | Press [2] |  |
|  | Press [4] |  |
|  | For Then A List of All PLUs Press [1] A Range of PLUs Press [2] Note: If ALL is chosen, skip to step #7 |  |
|  | If Selective was chosen: To List By Then Code Range Press [1] Department Press [2] |  |
|  | Enter the beginning PLU #, press [ENTER] then enter the end PLU # and [ENTER]. OR Enter the department number then press [ENTER]. |  |
|  | Stop. |

#### Department Print

| Information | This sub-menu allows you to print the Departments currently programmed in the terminal. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Press [5] |  |
|  | For Then A List of All Departments Press [1] A Range of Departments Press [2] |  |
|  | Stop. |

#### Receipt Print

| Information | This sub-menu allows you to print copies of receipts from closed journals. |
| --- | --- |

Note

The register must be closed in order to use this menu.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ECR Closed prompt. |  |
|  | Press [2] |  |
|  | Press [6] |  |
|  | Swipe the Manager Card. |  |
|  | Enter the Journal number that contains the desired transaction then press [ENTER] | Note: The current journal number is displayed. |
|  | Input the Transaction number and press [ENTER] |  |

Continued on next page

Print Receipt, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | If Then Journal & Transaction # are in the database The Receipt Copy will Print. Neither the Journal nor Transaction # are found in the database One of the following will be displayed: Note: Only the last closed journal is available in Stand Alone mode. |  |
|  | Stop. |

#### Change Discount

| Information | This sub-menu allows you to change the default discount percentage. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Press [7] |  |
|  | Input the new discount % then press [ENTER]. |  |
|  | Stop. |

#### Force Client

| Information | This menu option is used to upload Client information to Backend PC when the client parameters have not yet been defined. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Press [8] |  |
|  | Press [ENTER] |  |
|  | Stop. |

#### Set Communication Time

| Information | This menu option is used to set the time that the register communicates with the Backend PC. |
| --- | --- |

Note

This function is not supported in stand-alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Press [9] |  |
|  | Enter the time for the register to close the batch then press [ENTER]. |  |
|  | Stop. |

#### Set Communication Parameters

| Information | This menu option is used to set the parameters for communicating with the Backend PC. The settings available are: ( Phone (Number) ( Exchange Prefix |
| --- | --- |

Note

This function is not supported in stand-alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Use the [] key to scroll down to #10 Set Communication Parameters then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Enter the phone number. |  |
|  | Press [ENTER] |  |

Continued on next page.

Set Communications Parameters, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Press [2] then press [ENTER] |  |
|  | If required, enter the exchange prefix digit then press [ENTER] |  |
|  | Press [MENU/ESC] to exit. |
|  | Stop. |

#### Allow Unknown PLU

| Information | This sub-menu gives you the option of allowing or disallowing entry of an unknown PLU during a transaction or via the Store Inventory option. All unknown PLUs are assigned to Dept. 99. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [2] |  |
|  | Use the [] key to scroll down to 11. Allow Unknown PLU then press [ENTER]. |  |
|  | Swipe manager card. |  |
|  | Use the [] key to scroll down between Allow and Disallow. Press [ENTER] to select. |  |
|  | Press [ENTER] |  |
|  | Stop. |

#### Edit Journal Number

| Information | This sub-menu gives you the option changing the next Journal number. |
| --- | --- |

Note

The register must be closed to change the journal number.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from ECR Closed prompt. |  |
|  | Press [2] |  |
|  | Use the [] key to scroll down to 12. Edit Journal Number then press [ENTER]. |  |
|  | Swipe manager card. |  |
|  | Enter the new journal number then press [ENTER] |  |
|  | Stop. |

### Merchant Options

| Information | The third menu in the NURIT 2159 is the Merchant Options menu. It is divided into six sub-menus. |
| --- | --- |

#### Operation Mode

| Information | This function switches the register between NURIT Wed and Stand Alone Modes. Switching between modes deletes all of the register information (i.e. Cashier, Department, PLU and such). |
| --- | --- |

Note

The register must be closed to switch modes.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from ECR Closed prompt. |  |
|  | Press [3] |  |
|  | Press [ENTER] |  |
|  | Scroll to select the setting then press [ENTER]. |  |
|  | Stop. |

#### Debit Double Receipt

| Information | This function enables and disables the printing of a second Debit receipt. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [3] |  |
|  | Press [2] |  |
|  | Scroll to select option then press [ENTER] | Note: The current setting appears in parenthesis. |
|  | Stop. |

#### Invoice Mode

| Information | When Invoice Mode is enabled, the register will prompt for an invoice number when processing a transaction. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt |  |
|  | Press [3] |  |
|  | Press [3] |  |
|  | Swipe the Manager Card. |  |
|  | Scroll to select option then press [ENTER]. |  |
|  | Stop. |

#### Security Menu

| Information | The security menu allows the manager to set the security levels for different terminal functions. This menu contains (9) nine sub-menus. These menus are: Menu, Open Register, Close Register, Open Drawer, Void, General Refund, Change Discount, ECR Reports and Batch. |
| --- | --- |

##### Menu / Batch

| Information | These menus allow the user to restrict access to the ECR MAIN MENU or the Batch function. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [1] to restrict access to the Menu. OR Press [9] to protect the Batch function. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

##### Open / Close Register

| Information | These menus allow the user to restrict the ability to open and close the register. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [2] to restrict the ability to open. OR Press [3] to restrict the ability to close the register. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

##### Open Drawer

| Information | This menu allows the user to restrict the ability to open the register draw. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [4] to restrict the ability to open the register draw. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

##### Void / General Refund

| Information | These menus allow the user to restrict the ability to process a Void or General Refund transaction. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [5] to restrict Void transactions. OR Press [6] to restrict General Refunds. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

##### Change Discount

| Information | This menu allows the user to restrict the ability to change the register discount percentage. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [7] to restrict the ability to change the discount percentage. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

##### ECR Reports

| Information | This menu allows the user to restrict the ability to print any of the ECR Reports. The available options are No Security, Employee and Manager Only. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [4] |  |
|  | Swipe the Manager Card. |  |
|  | Press [8] to restrict the ability to print ECR Reports. |  |
|  | Use the arrow keys [] or [] to scroll through the choices. Press [ENTER] to select. |  |
|  | Stop. |

#### Edit Menu

| Information | This menu allows you to edit: ( Header Text ( Trailer Text ( Hot Keys When the register is in Stand Alone Mode, the following options are also available: ( PLUs ( Departments ( Cashiers |
| --- | --- |

##### Edit Header / Trailer

| Information | The Header and Trailer text is the user-defined lines of text (five lines, 24 characters per line) that appear at the top of reports and at the top and bottom of transaction receipts. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from Ready prompt. |  |
|  | Press [3] |  |
|  | Press [5] |  |
|  | Press [1] to edit the Header. OR Press [2] to edit the Trailer. |  |
|  | Use the left and right arrow keys to move the cursor over the line to the text that you wish to edit. |  |
|  | Use the up and down arrow keys to through the text lines. |  |

Continued on next page.

Edit Header / Trailer, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | When the Cursor is blinking directly over the letter you wish to edit press the Number that corresponds to the desired letter. For Example: For the letters A, B, C you will press the #2, for the letters D, E, F you will press the #3, etc. |
|  | Press [ALPHA/COPY] until the desired letter is displayed. |
|  | Repeat steps 7-8 until you have made all the desired revisions. Press [MENU/ESC] when the text changes are complete. |
|  | Press [ENTER] |  |
|  | Stop. |

##### Edit Hot Keys

| Information | This sub-menu is used to set the (8) eight Hot Keys. Only PLUs and Departments can be set as Hot Keys. Before you can set the hot keys, the terminal must be programmed with PLUs or Departments. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu, press [3] to edit the Hot Keys. |  |
|  | Press [DEPT] to assign a department OR Press [PLU] to assign a PLU. |  |
|  | For Then Department Hot Key Input the department number then press [ENTER] PLU Hot Key Input the PLU number then press [ENTER] |  |
|  | Press [ENTER]. |  |
|  | Press [ENTER] again to advance and set Hot Key # 2. Repeat steps to edit all hot keys. |
|  | Stop. |

##### Creating New PLUs

| Information | This sub-menu is used to manually create PLU numbers and names. When using a web or back end solution PLU’s can NOT be entered manually at the terminal level. |
| --- | --- |

Note

The function is supported in Stand Alone Mode Only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [4]. |  |
|  | If Then No PLUs have been entered Input the PLU number then press [ENTER] or scan the PLU Other PLUs exist Input the PLU number then press [ENTER] or scan the PLU |  |
|  | Press [ENTER] |  |
|  | Enter the PLU name by pressing the number that corresponds to the desired letter then pressing [ALPHA/COPY] for the letter. Press [ENTER] when the name is complete. For Example: For the letters A, B, C you will press the #2, for the letters D, E, F you will press the #3, etc. |  |
|  | Input the new PLU price and press [ENTER] |  |
|  | If you wish to add this PLU to a Department, input the department number and press [ENTER] |  |

Continued on next page

Creating New PLUs, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Use number keys [1], [2], [3], and [4] to turn the Taxes and Hot Keys On/Off. Note: a ‘+’ indicates the function is enabled and a ‘-‘ indicates it is disabled. |  |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

##### Editing Existing PLUs

| Information | This sub-menu is used to edit existing PLU numbers and names. |
| --- | --- |

Note

The register must be closed to edit existing PLUs. This function is supported in Stand Alone Mode only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [4]. |  |
|  | Use the up and down arrow keys to scroll through the existing PLUs. | Note: The programmed PLU number and name will appear on the display. |
|  | Press [ENTER] to select the PLU to be modified. |  |
|  | Use the left and right arrow keys to position the cursor/underline under the character to be modified. |  |
|  | When letter you wish to edit is underlined press the Number that corresponds to the desired letter. Delete with unwanted letter with the [CANCEL/VOID] key For Example: For the letters A, B, C you will press the #2, for the letters D, E, F you will press the #3, etc. |
|  | Press [ALPHA/COPY] until the desired letter is displayed. Repeat steps 4-6 until you have finished modifying the PLU. Press [ENTER]. |  |
|  | Input the new PLU price and press [ENTER] |  |
|  | If you wish to add this PLU to a Department, input the department number and press [ENTER] |  |

Continued on next page

Editing Existing PLUs, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Use number keys [1], [2], [3], and [4] to turn the Taxes and Hot Keys On/Off. |  |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

##### Creating New Departments

| Information | This sub-menu is used to manually create new Departments. When using a web or back end solution Departments CANNOT be entered manually at the terminal level. |
| --- | --- |

Note

The function is supported in Stand Alone Mode Only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [5]. |  |
|  | If Then No Departments have been entered Input the Department number then press [ENTER] Other Departments exist Input the Department number then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Enter the Department name by pressing the number that corresponds to the desired letter then pressing [ALPHA/COPY] for the letter. Press [ENTER] when the name is complete. |  |
|  | Use number keys [1], [2], [3], and [4] to turn the Taxes and Hot Keys On/Off. |  |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

##### Editing Existing Departments

| Information | This sub-menu is used to edit existing Departments. |
| --- | --- |

Note

The register must be closed to edit existing Departments. This function is supported in Stand Alone mode only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [5]. |  |
|  | Use the up and down arrow keys to scroll through the existing Departments. | Note: The programmed Department will appear on the display. |
|  | Press [ENTER] to select the Department to be modified. |  |
|  | Use the left and right arrow keys to position the cursor/underline under the character to be modified. |  |
|  | When the letter you wish to edit is underlined press the Number that corresponds to the desired letter. Delete unwanted letter with the [CANCEL/VOID] key. For Example: For the letters A, B, C you will press the #2, for the letters D, E, F you will press the #3, etc. |
|  | Press [ALPHA/COPY] until the desired letter is now displayed. |  |
|  | Repeat steps 4-6 until you have finished modifying the PLU. Press [ENTER] |

Continued on next page

Editing Existing Departments, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Use number keys [1], [2], [3], and [4] to turn the Taxes and Hot Keys On/Off. |  |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

##### Creating New Cashiers

| Information | This sub-menu is used to manually create new Cashiers. |
| --- | --- |

Note

When using a web or back end solution Cashiers can NOT be entered manually at the terminal level.

The register must be closed to create new cashiers.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [6]. |  |
|  | If Then No Cashiers have been entered Input the Cashier number then press [ENTER] Other Cahsiers exist Input the Cashier number then press [ENTER] |  |
|  | Press [ENTER] |  |
|  | Enter the Cashier name by pressing the number that corresponds to the desired letter then pressing [ALPHA/COPY] for the letter. Press [ENTER] when the name is complete. |  |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

##### Editing Existing Cashiers

| Information | This sub-menu is used to edit existing Cashiers. |
| --- | --- |

Note

The register must be closed to edit existing cashiers. This function is supported in Stand Alone mode only.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Edit Menu press [6]. |  |
|  | Use the up and down arrow keys to scroll through the existing Cashiers. | Note: The programmed Cashier will appear on the display. |
|  | Press [ENTER] to select the Cashier to be modified. |  |
|  | Use the left and right arrow keys to position the cursor/underline under the character to be modified. |  |
|  | When the letter you wish to edit is underlined press the Number that corresponds to the desired letter. Delete unwanted letter with the [CANCEL/VOID] key. For Example: For the letters A, B, C you will press the #2, for the letters D, E, F you will press the #3, etc. |
|  | Press [ALPHA/COPY] until the desired letter is now displayed. |
|  | Repeat steps 4-6 until you have finished modifying the Cashier. Press [ENTER] |
|  | To Then Print the changes Press [ENTER] To bypass printing the changes Press [MENU/ESC] |  |
|  | Stop. |

#### Tax Menu

| Information | This menu allows you to edit the: ( Tax % ( Tax Name |
| --- | --- |

##### Set Tax %

| Information | This sub-menu allows you to set the (3) three available tax percentages. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [3] |  |
|  | Press [6] |  |
|  | Press [ENTER]. |  |
|  | Press [ENTER] |  |
|  | Input the new tax amount and Press [ENTER] |
|  | Repeat step 6 for Tax2 and Tax3 if desired. |
|  | Stop. |

##### Tax Name

| Information | This sub-menu allows you to modify the three available tax names. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [3] |  |
|  | Press [6] |  |
|  | Press [2] then [ENTER]. |  |
|  | Press [ENTER] |  |
|  | Input the new tax name and press [ENTER] |  |
|  | Repeat step 6 for Tax2 and Tax3 if desired. |
|  | Stop. |

### System Options

| Information | This menu consists of three sub-menus, which allow the user to adjust several terminal functions. The available menus are: ( Set Time/Date ( Site ID ( Reset Database |
| --- | --- |

#### Set Time/Date

| Information | This sub-menu allows the user to set the terminal Date and Time. Even though the time is displayed on the screen with an AM or PM following, the time must be entered in Military or 24-hour format. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the ready prompt. |  |
|  | Press [4] |  |
|  | Press [ENTER] |  |
|  | Press [ENTER]. |  |
|  | Enter the current date in MMDDYY format. |  |
|  | Input the current date in hhmm format. The time must be entered in 24-hour/Military time. |  |
|  | Stop. |

#### Site ID

| Information | This sub-menu is used to change the Manager Card number that the terminal recognizes to a different card or number. The register must be closed for this function. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the closed prompt. |  |
|  | Press [4] |  |
|  | Press [2] |  |
|  | Press [ENTER] Note: The current Site ID will be displayed. |  |
|  | Swipe old manager card. |  |
|  | Swipe the new Manager Card. OR Press [MENU], enter the new Site ID then press [ENTER]. |  |
|  | Stop. |

#### Reset the Database

| Information | This menu is used to reset the terminal database. The register must be closed for this function. This function clears the Cashier, Department and PLU databases. |
| --- | --- |

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the closed prompt. |  |
|  | Press [4] |  |
|  | Press [3] |  |
|  | Swipe Manager Card. |  |
|  | Press [ENTER]. |  |
|  | Press [MENU/ESC] |  |
|  | Stop. |

### BarCode Functions

| Information | Any one of five types of bar codes can be printed using the BarCode Function. The register must be closed to access this function. The five types of bar-codes are: ( EAN-13 ( EAN-8 ( UPC-A ( UPC-E ( USD-3 |
| --- | --- |

#### Print BarCodes

| Step | Action | Display |
| --- | --- | --- |
|  | Press [MENU/ESC] from the closed prompt. |  |
|  | Press [5] |  |
|  | Press [ENTER] |  |
|  | Use the up [] and down [] arrows to scroll through the available bar code types, press [ENTER] to select. |  |
|  | Enter the bar code number (maximum number of digits is dependent upon the type) then press [ENTER]. The requested bar code will print. |  |
|  | To print more of the same code, press [ENTER] OR Press [MENU/ESC] to exit. |  |
|  | Stop. |

### POS Functions

| Information | The POS Functions menu is primarily used for Development and Troubleshooting purposes. |
| --- | --- |

Note

The register must be closed to access the POS Function menu.

### POS Communications

| Information | The POS Communications menu is used the set the telephone line parameters for communication to the Host Processors. |
| --- | --- |

#### Line Parameters

##### Maximum Retries

Note

This parameter sets the number of times the register will attempt to contact the Host. If the number in the Number of Attempts (LandLine and Radio only) field in the Host Access Parameters window in the NCC is three, a Maximum Retries value of one will cause the process of three retries to be repeated once. Maximum Retries affects all communication.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [6] |  |
| 4. | Press [ENTER] |  |
| 5, | Press [ENTER] |  |
| 6. | Enter the number of times the terminal should dial each of the three phone numbers then press [ENTER]. |  |
| 6. | Stop |

##### Dial Type

Note

This parameter toggles the terminal between Tone and Pulse dialing.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [6] |  |
| 3. | Press [ENTER] |  |
| 4. | Press [2] |  |
| 5. | Press [1] for Tone dialing or press [2] for Pulse dialing. |  |
| 6. | Stop |

##### Dialing Prefix

Note

Use this function to enter a required dialing prefix.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [6] |  |
| 3. | Press [ENTER] |  |
| 4. | Press [3] |  |
| 5. | Enter the dialing prefix digit then press [ENTER] |  |
| 6. | Stop |

##### Phone Number Display

Note

The Phone # Display feature controls weather or not the phone number that the terminal is dialing is displayed on the screen while the terminal is dialing.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [6] |  |
| 3. | Press [ENTER] |  |
| 4. | Press [4] |  |
| 5. | Press [1] for Yes or press [2] for No. |  |
| 6. | Stop |

##### Break Mode

Note

Break Mode allows or does not allow the user to interrupt the process while the terminal is establishing communications with the host processor.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [6] |  |
| 3. | Press [ENTER] |  |
| 4. | Press [5] |  |
| 5. | Press [1] for ON or press [2] for OFF. |  |
| 6. | Stop |

### POS Reports

| Menu Description | The available reports in this Reports menu are concerned with all EDC types other than Cash. This generates a number of different report options: ( Default Report ( Current Report ( History Report ( Performance ( Report Setup |
| --- | --- |

| Report Types | You will be prompted in the Current Report sub-menu to choose a report type. When the settings are saved at the end of the Current Report process, the Report Type specified is the type of report printed for a Default Report and a Batch Report. Below is a list of report types and their definitions. |
| --- | --- |

| Report | Definition |
| --- | --- |
| Condensed Report | This type of report will print the transaction number, card type, transaction type, last four digits of the account number, and the amount of the sale. |
| Short Report | This type of report will print the transaction type and the amount of the sale. |
| Journal Report | This type of report will print a full copy of each transaction. |
| Totals Only | This type of report will print daily totals only. |

Note

Print a Journal Report to obtain the full 16-digit account number for Credit transactions.

#### Default Report

Note

This report lists the register’s daily Credit, Debit, Check, Gift and Phone card transactions in a format that is configured in the Current Report menu. Current Report is described on the next page.

| Step | Action | Display |
| --- | --- | --- |
| 1. | Press [MENU/ESC] from the ready prompt. |  |
| 2. | Press [8] |  |
| 3. | Enter the eight digit daily password (MMDDYYYY) or User specified password then press [ENTER] |  |
| 4. | Press [ENTER] |  |
| 5. | Stop. |

#### Current Report

Note

This report lists the register’s daily card transactions in a format that can be customized. You can choose this report as your default report by saving it when the terminal asks: “Save as Default?” If yes, press ENTER, if no then press MENU.

| Step | Action | Display |
| --- | --- | --- |
| 1. | From the POS Reports menu, press [2] to select Current Report. |  |
| 2. | Use the [] and [] keys to scroll through the Report Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
| 3. | Scroll through the EDC Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
| 4. | Scroll through the Card Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
| 5. | Scroll through Sorting Options, [ENTER] to select. OR Press the number corresponding with your selection. |  |

Continued on next page.

Current Report, Continued

| Step | Action | Display |
| --- | --- | --- |
| 6. | Scroll through the Transaction Type options, [ENTER] to select. OR Press the number corresponding with your selection |  |
| 7. | To Then Save this as your default report Press [ENTER] Keep your current default setting Press [MENU] |  |
| 8. | Stop. |

#### History Reports

Note

The history reports prints batch totals for the preceding 300 batches. If there are three different EDC/Payment (Cash and Coupon not included) types programmed into the register, each of the three creates its own batch information. This means that a History Report would be able to print information for the last 100 days.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Reports menu, press [3] to select History Report |  |
|  | Using the numeric keypad input the batch date you would like the report to begin with: Press [ENTER] |  |
|  | Using the numeric keypad input the batch date you would like the report to end with: Press [ENTER] |  |
|  | Press the number corresponding with the type of History Report, Total or Per Batch. |  |
|  | Scroll through the EDC Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
|  | Scroll through the Card Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |

Continued on next page.

History Report, Continued

| Step | Action | Display |
| --- | --- | --- |
|  | Scroll through the Transaction Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
|  | Stop. |

#### Performance Report

Note

This function prints a report listing the percentages of denials, approvals, swipes, manual entries and other register statistics.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Reports menu, press [6] to select Performance |  |
|  | Scroll through the EDC Type options, [ENTER] to select. OR Press the number corresponding with your selection. |  |
|  | The Performance Report will print. To Then Reset the Performance Report Press [ENTER] Keep the Default Report data Press [MENU] |  |
|  | Stop. |

#### Report Setup – Printing Visa/MC Options

Note

This function configures the register to print Visa and MasterCard transactions together (the default setting) or separately. Report must be sorted by Card Type to see separate listing.

| Step | Action | Display |
| --- | --- | --- |
|  | From the Reports menu, press [8] to select Report Setup |  |
|  | Press [ENTER] to select 1. Visa/MasterCard Setup. |  |
|  | Use the [] and [] keys to select if you would like Visa and MasterCard printing together or separately then press [ENTER]. OR Press the number corresponding with your selection |  |
|  | Stop. |

## Communication Utilities

#### Batch to Host

| Information | Each EDC can be batched separately or together using the Batch To Host function in the Communication Utilities menu. The batches can also be closed either separately or together when the register is closed. Depending upon the Host Processor, some additional reports and functions are available in the Batch To Host menu. |
| --- | --- |

Note

The register must be closed to access this function.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [ENTER] |  |
|  | Use the [] and [] keys to make your selection then press [ENTER]. OR Press the number corresponding with your selection |  |
|  | The register will dial out to the Host Processors and close the batches. |  |
|  | Stop. |

#### Transaction Upload

| Information | This function uploads the transactions from the register to the back-end software. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [2] |  |
|  | The register will briefly display a message while uploading. |  |
|  | Stop. |

#### PLU Download

| Information | This function downloads the PLU information from NURIT Store to the register. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [3] |  |
|  | The register will briefly display a message while loading. |  |
|  | Stop. |

#### Department Download

| Information | This function downloads the Department information from NURIT Store to the register. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [4] |  |
|  | The register will briefly display a message while loading. |  |
|  | Stop. |

#### Cashier Download

| Information | This function downloads the Cashier information from NURIT Store to the register. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [5] |  |
|  | The register will briefly display a message while loading. |  |
|  | Stop. |

#### Client Download

| Information | This function downloads the Client information from NURIT Store to the register. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [6] |  |
|  | The register will briefly display a message while loading. |  |
|  | Stop. |

#### Auto Load

| Information | This function downloads the PLU, Department, Cashier and Client information from NUIRIT Store to the register. This function must be performed after the register is programmed or has its programming updated. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [7] |  |
|  | The register will briefly display a message while loading. |  |
|  | Stop. |

#### Employee Report

| Information | Prints a report of the cashier’s Time and Attendance.. |
| --- | --- |

Note

The register must be closed to access this function. This function is not supported in Stand Alone mode.

| Step | Action | Display |
| --- | --- | --- |
|  | Press [COMM UTILITY] from the ECR Closed prompt. |  |
|  | Press [8] |  |
|  | The register will briefly display a message while retrieving the information. After the information has been retrieved, the report will print. |  |
|  | Stop. |

## NURIT 2159 QUICK REFERENCE GUIDE

To access the menu, press [MENU/ESC].  Use this key to enter & exit out of the menu.  Use [▲] and [▼] keys to scroll up & down through menu options.

| ECR MAIN MENU | SUB-MENU | FUNCTION DESCRIPTION |
| --- | --- | --- |
| 1. REPORTS | 1. X/Z Defaults | Sets defaults for X and Z Reports |
|  | 2. Print X Report | Prints the X Report |
|  | 3.Settings | Prints a report listing the register’s settings |
|  | 4. Non Resettable | Prints the Non Resettable report |
|  | 5. Register Reports | Prints the PLU, Department, Cashier, and T & A Reports |
|  | 6. Periodical Report | Prints the hourly Periodical Report |
|  | 7. Cumulative Report | Prints the Cumulative Report |
|  | 8. Journal Report | Prints Journal Report. |
|  | 9. Display Transactions | Displays transactions in current or past journals |
| 2. ECR OPTIONS | 1. Delete Journal | Deletes the current Journal |
|  | 2. Delete PLU File | Delete the existing PLU database. |
|  | 3. Set HALO | Sets the maximum transaction amount. |
|  | 4. PLU Print | Prints a list of the current PLUs. |
|  | 5. Department Print | Prints a list of the current Departments |
|  | 6. Receipt Print | Prints a copy of a specified receipt |
|  | 7. Change Discount | Changes the current discount percentage |
|  | 8. Force Client | Force enter a new client not at the background PC. |
|  | 9. Set Communication Time | Sets the time to register will automatically batch |
|  | 19. Set Communication Parameters | Sets the communication parameters |
|  | 11. Allow Unknown PLU | Allow entry of an unknown PLU when entering a transaction |
|  | 12. Edit Journal Number | Changes the current journal number |
| 3. MERCHANT OPTIONS | 1. Operation Mode | Switches between Stand-Alone and NURIT WEB modes |
|  | 2. Double Receipt | Enable or Disable a second receipt on Debit transactions. |
|  | 3. Invoice Mode | Enable or Disable invoice Mode |
|  | 3. Security Menu | Contains security switches for Menu, Open Register, Close Register, Open Draw, Void, General Refund, Change Discount, ECR Report and Batch functions |
|  | 4. Edit | Enables the user to Edit the Header, Hot Keys, PLUs, Departments and Cashiers |
|  | 5. Tax Menu | Enables the user to set the three tax amounts and edit the tax names |
| 4. SYSTEM OPTIONS | 1. Set Time and Date | Sets Terminal’s Date (mm/dd/yy) and Time (hh:mm:00) |
|  | 2. Site ID | Change Site ID |
|  | 3. Reset Database | Reset terminal database |
| 5. BAR CODE FUNCTION | 1. Print Bar Cade | Prints five types of bar codes |
| 6. POS MENU | Programming and Troubleshooting Only |
| 7. POS COMMUNICATIONS | 1. Line Parameters | Sets the Maximum Retries; exchange Prefix; Dial Type; Phone Number Display and Break Mode |
| 8.POS REPORTS | 1.Default Report | Lists the current Credit, Debit, Check, Gift/Loyalty and Phone card transactions. |
|  | 2. Current Report | Sets the format for the Default Report |
|  | 3. History Report | Lists information for the last 300 closed batches |
|  | 4.Performance Report | Prints percentage of Approvals, Denials, Disconnects, Manual Entries and Swipes. |
|  | 5.Report Setup | Separates VISA and MasterCard transactions |

## Appendix A

# Lipman USA Licensing Agreement

Nurit 2159

END-USER LICENSE AGREEMENT FOR LIPMAN USA SOFTWARE

IMPORTANT-READ CAREFULLY: This Lipman End-User License Agreement (“EULA”) is a legal agreement between you (either an individual or a single entity) and Lipman USA, Inc. (“Lipman”) for the Lipman Software Product identified above, which may include associated media, printed materials, and “online” or electronic documentation (“Software Product”).  By installing, copying, or otherwise using the Software Product, you agree to be bound by the terms of this EULA.  If you do not agree to the terms of this EULA, do not install, copy or use the Software Product and return the product to our attention at the address set forth below for a full refund.

SOFTWARE PRODUCT LICENSE

The Software Product is protected by copyright laws and international copyright treaties, as well as other intellectual property laws and treaties.  The Software Product is licensed, not sold.

1.	GRANT OF LICENSE.  This EULA grants you the following rights:

* Software License.  Lipman grants you the non-exclusive right to make and use, solely in connection with your use of Lipman terminals, a number of  copies of the Software Product equal to the number of  Lipman [insert name of terminal] terminals validly purchased by you.  You may also make copies of the Software Product for backup and archival purposes.

* Distribution.  Lipman grants you a non-exclusive, royalty-free right to reproduce and distribute an unlimited number of copies of the Software Product, solely for use in connection with Lipman terminals, provided that you:  (a) distribute the Software Product in object code form only as part of a software product created by you for use with Lipman terminals, that adds significant and primary value to the Software Product (the “Licensed Product”); provided such Licensed Product complies with all applicable laws, rules and regulations, including without limitation, all VISA, MasterCard and other association rules and regulations; (b) do not use Lipman’s name, logo, or trademarks to market the Licensed Product; (c) will not permit further distribution of the Software Product by your end-user customers; (d) include a valid copyright notice on the Licensed Product sufficient to protect Lipman’s copyright in the Software Product; (e) distribute and license the use of the Licensed Product to end users only pursuant to your end user license agreement; (f) indemnify, hold harmless, and defend Lipman from and against any claims or lawsuits, including attorney’s fees, that arise or result from the use or distribution of your Licensed Product; (g) otherwise comply with the terms of this EVLA; and (h) agree that Lipman reserves all rights not expressly granted.  No license is granted to you in the source code of the Software Product.

Continued on next page

Lipman USA Licensing Agreement, Continued

2.	DESCRIPTION OF OTHER RIGHTS AND LIMITATIONS.

Not for Redistribution Software.  If the Software Product is labeled “Not for Redistribution” or “NFR,” then, notwithstanding other sections of this EULA, you may not resell, sublicense, or otherwise transfer for value, the Software Product by itself or as part of a Licensed Product.

* Maintenance of Copyright Notices.  You must not remove or alter any copyright notices on all copies of the Software Product.

* Limitations on Reverse Engineering, Decompilation, and Disassembly.  Neither you nor your end-user customers may reverse engineer, decompile, disassemble or otherwise attempt to discover the source code of the Software Product, except and only to the extent that such activity is expressly permitted by applicable law notwithstanding this limitation.

*Separation of Components.  The Software Product is licensed as a single product.  Its component parts may not be separated for use on more than one terminal.

* Performance or Benchmark Testing.  You may not disclose the results of any benchmark test of the Software Product to any third party without Lipman’s prior written approval.

* Support Services.  Lipman may provide you with support services related to the Software Product (“Support Services”), use of Support Services is governed by the Lipman policies and programs described in the user manual, in “online” documentation, and/or in other Lipman-provided materials.  Any supplemental software code provided to you as part of the Support Services shall be considered part of the Software Product and subject to the terms and conditions of this EULA.  With respect to technical information you provide to Lipman as part of the Support Services, Lipman may use such information for its business purposes, including for product support and development.  Lipman will not utilize such technical information in a form that personally identifies you.

* Software Transfer.  You may permanently transfer all of your rights under this EULA (i) only in conjunction with a permanent transfer of your validly purchased Lipman terminals; (ii) provided you retain no copies; (iii) you transfer all of the Software Product (including all component parts, the media and printed materials, and any upgrades); and (iv) the recipient agrees to the terms of this EULA.  If the Software Product is an upgrade, any transfer must include all prior versions of the Software Product.

* Termination.  Your rights under this EULA terminate upon the termination of your right to use the Lipman terminal being used in connection with the Software Product.  Without prejudice to any other rights, Lipman may terminate this EULA if you fail to comply with the terms and conditions of this EULA.  In such event, you must destroy all copies of the Software Product and all of its component parts.

Continued on next page

Lipman USA Licensing Agreement, Continued

- UPGRADES

If the Software Product is labeled as an upgrade, you must be properly licensed to use a product identified by Lipman as being eligible for the upgrade in order to use the Software Product.  A Software Product labeled as an upgrade replaces and/or supplements the product that formed the basis for your eligibility for the upgrade.  You may use the resulting upgraded product only in accordance with the terms of this EULA.  If the Software Product is an upgrade of a component of a package of software programs that you licensed as a single product, the Software Product may be used and transferred only as part of that single product package and may not be separated for use on more than one terminal.

- COPYRIGHT

All title, including but not limited to copyrights, in and to the Software Product and any copies thereof are owned by Lipman or its suppliers.  All title and intellectual property rights in and to the content which may be accessed through use of the Software Product is the property of the respective content owner and may be protected by applicable copyright or other intellectual property laws and treaties.  This EULA grants you no rights to use such content.

- U.S. GOVERNMENT RESTRICTED RIGHTS

The Software Product is provided with RESTRICTED RIGHTS.  Use, duplication, or disclosure by the Government is subject to restrictions as set forth in subparagraph (c)(1)(ii) of the Rights in Technical Data and Computer Software Clause at DFARS 252.227-7013 or subparagraphs (c)(1) and (ii) of the Commercial Computer Software Restricted Rights at 48 CFR 52.227-19, as applicable.  Manufacturer is Lipman USA, Inc., 50 Gordan Drive, Syosset, New York 11791.

- EXPORT RESTRICTIONS

You agree that you will not export or re-export the Software Product to any country, person, entity or end user subject to U.S.A. export restrictions.  Restricted countries currently include, but are not necessarily limited to Cuba, Iran, Iraq, Libya, North Korea, Sudan, and Syria.  You warrant and represent that neither the U.S.A. Bureau of Export Administration nor any other federal agency has suspended, revoked or denied your export privileges.

- NO WARRANTIES.

Lipman expressly disclaims any warranty for the Software Product.  THE SOFTWARE PRODUCT IS PROVIDED “AS IS” WITHOUT WARRANTY OR CONDITION OF ANY KIND, EITHER EXPRESS OR IMPLIED, INCLUDING, WITHOUT LIMITATION, THE IMPLIED WARRANTIES OF MERCHANTABILITY, FITNESS FOR A PARTICULAR PURPOSE, OR NON-INFRINGEMENT.  THE ENTIRE RISK ARISING OUT OF USE OR PERFORMANCE OF THE SOFTWARE PRODUCT REMAINS WITH YOU.

Continued on next page

Lipman USA Licensing Agreement, Continued

- LIMITATION OF LIABILITY

In no event shall Lipman or its suppliers be liable for any damages whatsoever (including, without limitation, damages for loss of business profits, consequential or incidental damages, business interruption, loss of business information, or any other pecuniary loss or expense) arising out of the use of or inability to use the Software Product, even if Lipman has been advised of the possibility of such damages.  Because some states and jurisdictions do not allow the exclusion or limitation of liability for consequential or incidental damages, the above limitation may not apply to you.

MISCELLANEOUS

This EULA is governed by the laws of the State of New York, excluding the application of its conflict of laws rules.  In the event of any dispute arising from or relating to this EULA, the parties hereto irrevocably consent to the personal jurisdiction of the courts located in New York, New York, which shall be the exclusive venue for any such dispute.  The United Nations’ Convention on International Sale of Goods does not apply.  This EULA sets forth the entire understanding and agreement between you and Lipman and may be amended only in a writing signed by both parties.

# Footnotes

This is a daily report of each PLU sold.  It will print the number of PLUs sold, and the dollar amount.  It can be printed as a stand-alone report and included on an X or Z report.

The Department report gives you the totals of each department for the day.  It will print the quantity of items sold in each department, total amount, and percentage of sales.  It can be printed as a stand-alone report and included on an X or Z report.

The Cashier report gives the totals summary for each cashier.  It shows the quantity of transactions done by each cashier, total amount, and the percentage of total sales.  It can be printed as a stand-alone report and included on an X or Z report.

# Comments

Could not test Time & Attendance.

What is the difference between Host Parameter Clear Database and System Option Reset Database?

# Text boxes

### Draft Copy

Alphanumeric Keys

Multifunction Hot Keys

ECR CLOSED

12/05/05     08:58 AM

Manager Card or

ESC for Password

CASH REGISTER

OPENING

OPENING BANK

0.00

DISCOUNT %

0.00

CASHIER ID

READY

12/05/05     09:00 AM

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

ECR OPENED

12/05/2005    9:00 AM

JOURNAL #	1

RGSTR #	2292491

OPENING BANK	100.00

DISCOUNT	5.00%

NURIT WEB MODE

READY

12/05/05     11:25 AM

Manager Card or

ESC for Password

DRAWER

1. Open Drawer

READY

12/05/05     11:25 AM

PAID IN

0.00

REASON ?

Manager Card or

ESC for Password

READY

12/05/05     11:25 AM

PAID OUT

0.00

REASON ?

Manager Card or

ESC for Password

READY

12/05/05     11:25 AM

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

PAID OUT

12/05/2005  01:20 PM

Amount	100.00

Reason	EXCESS CASH

APPROVED by MERCHANT

Cshr #1	Sasha

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

PAID IN

12/05/2005  01:20 PM

Amount	25.00

Reason	LOW CASH

APPROVED by MERCHANT

Cshr #1	Sasha

READY

12/05/05     10:05 PM

Manager Card or

ESC for Password

BATCH CLOSE ?

ENTER-Yes, ESC-No

CHOOSE HOST:

1.ALL

Close Register

ENTER-Yes, ESC-No

ENSURE

SUFFICIENT PAPER

Repeat?

ENTER-Yes, ESC-No

PC COMMUNICATION

PROCESSING . . .

ECR CLOSED

12/05/05            10:10PM

EDC:				DEBIT

Trn		TP	Acct	$Amount

*************************

1		SL	1234	25.03

2		SL	2345	45.17

*************************

DEBIT Records:	2

DEBIT TOTAL:	70.20

TOTAL OF TRANSACTIONS

WITHOUT TIPS:	70.20

Incl. Cash Back	20.00

=========================

EDC:				GIFTCARD

Trn	Trans	Type	$Amount

*************************

1	RE	1234	25.03

2	IS	2345	50.00

3	AV	3456	30.00

4	IS	4567	60.00

5	VD	5678	0.00

6	BI	6789	50.00

*************************

GIFTCARD Records:	6

GIFTCARD TOTAL:	25.03

TOTAL OF TRANSACTIONS

WITHOUT TIPS:	25.03

=========================

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Batch Report

12/05/2005  10:00 PM

Manual Batch Utility:

Supported EDC Types

Close Batch

-------------------------

Supported Host Names and Merchant Parameters.

Batch	5

Response:	BATCH CLOSED

OR BATCH CLEARED

(Host Dependent)

Terminal Number:	2292491

-------------------------

EDC:	CREDIT

Trn	Crd	Tp	Acct	$Amount

*************************

1	M/C	SL	1234	25.03

2	VIS	VE	2345	50.00

3	AMX	SL	3456	123.45

4	M/C	TK	4567	50.00

5	M/C	SL	5678	115.88

*************************

CREDIT Records:	5

CREDIT TOTAL:	314.36

TOTAL OF TRANSACTIONS

WITHOUT TIPS:	314.36

=========================

EDC:	PHONECARD

Trn	Trans	Type	$Amount

*************************

1	PN	5678	40.00

2	CR	6789	30.00

*************************

PHONECARD Records:	2

PHONECARD TOTAL:	0.00

TOTAL OF TRANSACTIONS

WITHOUT TIPS:	0.00

=========================

EDC:			CHECK

Trn	Trans	Type	$Amount

*************************

1	SL		25.03

2	SL		35.00

*************************

CHECK Records:	2

CHECK TOTAL:		60.03

TOTAL OF TRANSACTIONS

WITHOUT TIPS:	60.03

=========================

Records:			17

Overall			469.62

End of Report

-------------------------

Dept. Report

REPORT’S TOTAL

TOTAL	4923.15

-------------------------

#:01	Grocery

TOTAL	3111.97

-------------------------

#:02	Dairy

TOTAL	323.44

-------------------------

#:03	Produce

TOTAL	392.11

-------------------------

#:04	Meat

TOTAL	534.76

-------------------------

#:05	Pet Prodts

TOTAL	79.98

-------------------------

#:06	Stationary

TOTAL	72.56

-------------------------

#:07	House Wares

TOTAL	203.16

-------------------------

#:08	Persnl Care

TOTAL	205.17

-------------------------

Cashier Rprt

Cshr # 1	Sasha

TOTAL AMOUNT	4764.83

TOTAL AMOUNT TRANS	267

CHARGE AMOUNT	4764.83

CHARGE AMOUNT TRANS	267

REFUND AMOUNT	0.00

CASH	2762.38

CHECK	42.00

CREDIT	947.12

DEBIT	1045.99

EBT	125.66

-------------------------

-------------------------

Journal Rprt

Jrnl #11	Tr #1

Unique TrNo

001001953843051207171729

12/05/05    09:05 AM

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*000000

Soda	3.49

txExc23	*00000056789012

Candy	2.29

txExc3	*00000067890123

Pens	5.59

Ntx	*00000078901234

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CASH		30.00

CHANGE		2.29

-------------------------

Jrnl #11	Tr #2

Unique TrNo

001001953843051207171729

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Z report

JRNL#00008 12/05/05 08:55

RGSTR #	2292491

NUMBER OF TRANS:	267

=========================

Cumultv. Rprt

REPORT’S TOTALS

TOTAL AMOUNT	4923.15

TOTAL AMOUNT TRANS	267

CHARGE AMOUNT	4923.15

CHARGE AMOUNT TRANS	267

REFUND AMOUNT	0.00

CASH	2762.38

CHECK	42.00

CREDIT	947.12

DEBIT	1045.99

EBT	125.66

Cash in Drawer	2682.38

OPENING BANK	200.00

DRAWER INCOME	2762.38

DRAWER OUTCOME	280.00

DRAWER OPENED (TIMES)	201

INCOM. TAX1	85.12

INCOM. TAX2	52.87

INCOM. TAX3	20.33

NET TAX	158.32

*************************

NET SALES	4764.83

*************************

If cashiers were changed without closing the register, a report for each cashier would be printed.

Remaining Journal Report lists all transaction information in format displayed above.

-------------------------

PLU Report

REPORT’S TOTAL

TOTAL	4764.83

-------------------------

*00000012345678

Milk

161.25

TOTAL ITEMS	125

-------------------------

*00000023456789

Bread	216.63

TOTAL ITEMS	87

-------------------------

Each PLU sold, the total quantity sold and the total amount is listed in the PLU Report for the closed register.

READY

12/05/05     11:25 AM

TEMP. CLOSED

11/20/05        11:25 AM

CASHIER ID

3

READY

11/20/05     11:25 AM

51000153.18

TOMATO JUICE

Exc123                       .90

.10

51000153.18

TOMATO JUICE

Exc123                      9.90

6PK SODA

Exc23                      3.49

.03

6PK SODA

Exc23                     10.47

MILK QT

Exc123                     1.29

.02

MILK QT

Exc123                      2.58

4.12

DEPARTMENT #

DAIRY

Exc123                      4.12

.02

4.12

DEPARTMENT #

DAIRY

Exc23                      8.14

5.66

GROCERY

Exc23                      5.66

.04

5.66

DEPARTMENT #

GROCERY

Exc23                      22.64

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #1	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122333

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000012345678

5X 1.29

Milk	6.45

Ntx	*00000023456789

Bread	2.49

Ntx	*00000023456789

5 X 2.49

Bread	12.45

05 txExc3	Pet Prodts

4.12

05 txExc3	Pet Prodts

2 X 4.12	8.24

03 Ntx	Produce

3.45

03 Ntx	Produce

2 X 3.45		6.90

Items entered by Department.

Items entered by PLU.

MILK QT

Exc123                      2.58

ENTER VOID ITEM

MILK QT

Exc123-                    2.58

Ntx	*00000012345678

Milk	1.29

-------------------------

ITEM VOID

Ntx	*00000012345678

Milk	1.29

READY

11/20/05     11:25 AM

1. Gift Receipt

2. Receipt Copy

1. Last Receipt

2. Any Receipt

TRNS#

1. Last Receipt

2. Any Receipt

SUB TOTAL

26.22

PROCEED TO PMNT?

26.22

ENTR AMT + TENDR

27.71

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #4	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122356

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CASH		30.00

CHANGE		2.29

Cshr # 1		Sasha

SUB TOTAL

26.22

PROCEED TO PMNT?

26.22

CHOOSE TENDER

27.71

CREDIT . . . . . . SALE

ACCOUNT                -->

Scroll Response

123456

TEAR SLIP   ---->

Press any Key . . .

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #5	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122410

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CREDIT		27.71

Card Type:	VISA

Acc:		************1234

Entry:		Swiped

Auth Code:	123456

Response:	APPROVAL

I AGREE TO PAY ABOVE

TOTAL AMOUNT ACCORDING

TO CARD ISSUER AGREEMENT (MERCHANT AGREEMENT IF CREDIT VOUCHER)

X. . . . . . . . . . . .

SIGNATURE

Cshr # 1		Sasha

SUB TOTAL

26.22

PROCEED TO PMNT?

26.22

CHOOSE TENDER

27.71

DEBIT . . . . . . . SALE

ACCOUNT           -->

Cash Back:

0.00

Please Enter PIN

on the PIN Pad    >  >

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #6	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122499

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CREDIT		27.71

Acc:		************1234

Cash Back:	20.00

Total:		47.71

Reference No.:	654321

Auth Code:	123456

Response:	APPROVAL

Cshr # 1		Sasha

SUB TOTAL

26.22

PROCEED TO PMNT?

26.22

CHOOSE TENDER

27.71

SALE AMOUNT:

0.00

Enter MICR or

Use Check Reader

Enter Check Num:

CASHBACK AMOUNT:

0.00

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #7	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122566

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CHECK		27.71

Acc:		************1234

Auth ID:

APPROVE OFF-LINE

Cshr # 1		Sasha

SUB TOTAL

26.22

PROCEED TO  PMNT?

26.22

CHOOSE TENDER

27.71

EBT

27.71

EBT . . . . . . . . SALE

ACCOUNT           -->

1.FOOD STAMP

2.CASH BENEFIT

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #8	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122600

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

EBT		27.71

Acc:		************1234

Cash Back:	20.00

Total:		47.71

Reference No.:	654321

Auth Code:	123456

Response:	APPROVAL

Cshr # 1		Sasha

CHOOSE TENDER

27.71

TOTAL PAYMENT

1.50

COUPON

1.50

ENTER COUPON #

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #22	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122810

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

COUPON		2.00

12345678901234

COUPON		1.50

23456789012345

CASH		30.00

Cshr # 1		Sasha

CHOOSE TENDER

27.71

GIFT CARD

27.71

OPTICARD CARD

CLERK ID               --->

Programs:

1.Gift Card

Transactions:

1.REDEMPTION

Enter account

or swipe card . . .

27.71

NO                       YES

APPROVED

Press any key . . .

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #24	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122888

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

GIFT CARD	27.71

Acc: ***************8404

Auth Code

Response

Cshr # 1		Sasha

6PK 12OZ WATER

Exc23                      4.99

1-DSCNT IN %

2-DSCNT IN $

READY

12/05/05     11:25 AM

6PK 12OZ WATER

$Exc23                     4.75

SUB TOTAL

126.17

TEAR SLIP   ---->

Press any Key . . .

Press any key . . .

SUB TOTAL

119.86

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #21	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122750

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Discountable Tot:	26.22

DSCNT 5.00%	1.31

-------------------------

-------------------------

SUB TOTAL	24.91

Tax1	5.7500%	1.06

Tax2	2.2500%	0.29

Tax3	1.5000%	0.08

-------------------------

TOTAL		26.34

CASH		26.34

Cshr # 1		Sasha

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Tr #20	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122707

Cshr # 1

Ntx	*00000012345678

Milk	1.29

1.29 – 0.06

DSCNT 5.00%	1.23

Ntx	*00000023456789

Bread	2.49

2.49 – 0.25

DSCNT 10.00%	2.24

Sub Total Discount

Item Discount

GENERAL REFUND

12/04/05     11:33AM

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Refund

Tr #17	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122687

Cshr # 1

tx	*00000087654321

Book	9.99

-------------------------

SUB TOTAL	9.99

Tax1	5.7500%	0.57

Tax2	2.2500%	0.22

Tax3	1.5000%	0.15

-------------------------

TOTAL		10.93

CREDIT		10.93

Card Type:	VISA

Acc:		************1234

ENTRY:		Swiped

AuthCode:	123456

RESPONSE:	APPROVAL

I AGREE TO PAY ABOVE

TOTAL AMOUNT ACCORDING

TO CARD ISSUER AGREEMENT (MERCHANT AGREEMENT IF CREDIT VOUCHER)

X . . . . . . . . . . . .

SIGNATURE

(. . .). . . . . . . . .

PHONE NUMBER

Cshr # 1		Sasha

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Refund

Tr #16	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208122655

Cshr # 1

tx	*00000087654321

Book	9.99

-------------------------

SUB TOTAL	9.99

Tax1	5.7500%	0.57

Tax2	2.2500%	0.22

Tax3	1.5000%	0.15

-------------------------

TOTAL		10.93

CASH		10.93

X . . . . . . . . . . . .

SIGNATURE

(. . .). . . . . . . . .

PHONE NUMBER

Cshr # 1		Sasha

CASH

CREDIT

READY

12/05/05     11:25 AM

Void by CASH

27.71

.........................

YOUR BUSINESS

123 MAIN ST.

ANYTOWN, NY 11111

1-800-555-1234

Void

Tr #18	Jrnl #13

RGSTR #	22924991

12/06/2005   12:23 PM

Unique TrNo:

001001953843051208123100

Cshr # 1

Ntx	*00000012345678

Milk	1.29

Ntx	*00000023456789

Bread	2.49

txExc3	*00000034567890

Cat Food	2.59

tx	*00000045678901

Shampoo	5.29

txExc23	*00000056789012

Soda	3.49

txExc23	*00000067890123

Candy	2.29

txExc3	*00000078901234

Pens	5.59

Ntx	*00000089012345

Tuna	3.19

-------------------------

SUB TOTAL	26.22

Tax1	5.7500%	1.10

Tax2	2.2500%	0.31

Tax3	1.5000%	0.08

-------------------------

TOTAL		27.71

CASH		27.71

-------------------------

VOID by CASH	27.71

Cshr # 1		Sasha

FORCED SALE

12/04/05     11:33AM

6PK 12OZ WATER

Exc123                   4.99

CHOOSE TENDER

52.88

CREDIT . . . . FORCED

ACCOUNT          -->

ENTER AUTH. NO:

6PK 12OZ WATER

Exc123                   4.99

50.00

DEPARTMENT #

DEPARTMENT #

97

Prepaid Gift

Exc123                   50.00

CHOOSE TENDER

112.34

Start of

GIFT CARD Auth

OPTICARD

CLERK ID            --->

Programs:

1.Gift Card

Transactions:

2.ISSUANCE

Swipe Card

OPTICARD AMOUNT

0.00

$50.00

NO                 YES

APPROVED

PRESS ANY KEY

TO START REFUND

GENERAL REFUND

GENERAL REFUND

12/05/05      10:05AM

50.00

DEPARTMENT #

97

Prepaid Gift

Exc123                  50.00

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

2.ISSUANCE

Swipe Card:

OPTICARD AMOUNT

50.00

$50.00

NO                     YES

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

3.ADD VALUE

Swipe Card:

OPTICARD AMOUNT

50.00

$50.00

NO                     YES

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

4.VOID

Enter account

or swipe card:

AUTH. CODE:

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

5.BALANCE

Enter account

or swipe card:

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

6.BATCH ISSUE

Swipe card:

OPTICARD AMOUNT

0.00

$10.00

NO                   YES

Swipe Last Card:

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

7.POST AUTH

Enter account

or swipe card:

AUTH. CODE:

OPTICARD AMOUNT

0.00

$10.00

NO                    YES

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

1.Gift Card

Transactions:

8.TRANSFER

Enter account

or swipe card:

Swipe New Card:

APPROVED

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

2.Loyalty

Transactions:

1.VOID

Enter account

or swipe card:

AUTH. CODE:

APPROVED

TEAR SLIP     ---->

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

2.Loyalty

Transactions:

2.BALANCE

Enter account

or swipe card:

APPROVED

TEAR SLIP     ---->

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

2.Loyalty

Transactions:

3.POST AUTH

Enter account

or swipe card:

AUTH. CODE:

OPTICARD AMOUNT

0.00

$10.00

NO                    YES

APPROVED

TEAR SLIP     ---->

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

2.Loyalty

Transactions:

4.TRANSFER

Enter account

or swipe card:

Swipe New Card:

APPROVED

TEAR SLIP     ---->

Press any Key . . .

READY

12/14/05     02:15 PM

OPTICARD

CLERK ID      --->

Programs:

2.Loyalty

Transactions:

5.ADD POINTS

Enter account

or swipe card:

OPTICARD AMOUNT

50.00

$50.00

NO                     YES

APPROVED

TEAR SLIP     ---->

Press any Key . . .

READY

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

1.X/Z Defaults

Journal Report

>OFF

Journal Report

>ON

Cumulative Rprt

>ON

READY

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

2.Print X Report

ENSURE

SUFFICIENT PAPER

READY

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

3.Settings

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

4.Non Resettable

READY

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

5.Register Rprts

Register Rprts

1.PLU Report

READY

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

6.Periodical Rpt

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

7.Cumulative Rpt

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

1.Reports

REPORTS:

8.Journal Rpt

READY

12/05/05      10:03 PM

ECR MAIN MENU:

1.Reports

REPORTS:

9.Display trans

Enter Jrnl #

Enter Trans #

Transaction #2

Sale

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR Options:

1.Delete Journal

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR Options:

2.Delete PLU file

Manager Card or

ESC for Password

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

3.Set Halo

TRANS. HALO

400000.00

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

4.PLU print

1-All

2-Selective

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

5.Dept print

1-All

2-Selective

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

6.Receipt print

Manager Card or

ESC for Password

JOURNAL #

34

TRNS #

1

SPECIFIED TRANS

NOT FOUND

PRINTING

OR

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

7.Discount

Discount %

0.00

READY

12/05/05      10:03 PM

ECR MAIN MENU

2.ECR Options

ECR OPTIONS

8.Force Client

FORCE ENTRY ?

ENTR-Yes, ESC-No

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

9.Set Comm. Time

SET BATCH TIME:

00:00

READY

12/05/05      10:03 PM

ECR MAIN MENU:

2.ECR Options

ECR OPTIONS:

10.Set Comm. Param

PARAMS (MODEM)

1.Phone>

Enter Phone Num:

PARAMS (MODEM)

1.Phone> 18005551

PARAMS (MODEM)

2.Exchange Pref >

Exchange Prefix:

ECR CLOSED

12/05/05      10:03 PM

Manager Card or

ESC for Password

READY

12/05/05      10:03 PM

ECR MAIN MENU

2.ECR Options

ECR OPTIONS

11.Alw unknwn PLU

UNKNWN PLU ENTRY

1.Allow

ARE YOU SURE?

ENTER=Yes, ESC=No

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

2.ECR Options

ECR OPTIONS

12.Edit Journal#

Manager Card or

ESC for Password

New Journal #

27

READY

12/05/05      10:03 PM

ECR MAIN MENU

3.Merch. Options

MERCH. OPTIONS

2.Double Receipt

00001234567890

BREAD

Double Rct (ON):

1.OFF

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

1.Invoice Mode

Manager Card or

ESC for Password

INVOICE MODE:

1.Off

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

1.Menu

Menu:

1.No Security

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

2.Open Register

Open Register:

1.No Security

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

4.Open Drawer

Open Drawer

1.No Security

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

5.Void

Void

1.No Security

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

7.Discnt. Chng

Discnt Chng

1.No Security

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

4.Security Menu

Manager Card or

ESC for Password

SECURITY SWITCH:

8.ECR Reports

Open Register:

1.Always Enabled

READY

12/05/05      10:03 PM

ECR MAIN MENU:

3.Merch. Options

MERCH. OPTIONS:

5.Edit

EDIT MENU

1.Edit Header

LOGO EDITOR   1   N

█      MY BUSINESS

LOGO EDITOR   2   N

█      MY ADDRESS

SAVE CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

3.Edit Hot Keys

HK1 Dept Null

P Null

ENTER PLU:

ENTER DEPT. #:

HK1

Overwrite Dept (PLU)

EDIT MENU

4.Edit PLU

NO DATA

* 00001234567890

BREAD

Not Found in DB

Create?

00123456789012

ENTER PRICE:

0.00

Department #

TX1+      TX2+      TX3+

HOT+                ENTER

PRINT CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

4.Edit PLU

* 00123456789012

MILK

00001234567890

BPEAD

00001234567890

BPEAD

ENTER PRICE

0.00

DEPARTMENT #

TX1+      TX2+      TX3+

HOT+                ENTER

PRINT CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

5.Edit Department

NO DATA

DEPARTMENT # 1

GROCERY

Not Found in DB

Create?

DEPARTMENT #10

TX1+      TX2+      TX3+

HOT+                ENTER

PRINT CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

5.Edit Department

DEPARTMENT # 1

GROCERY

DEPARTMENT # 4

PRODUSE

DEPARTMENT # 4

PRODUSE

TX1+      TX2+      TX3+

HOT+                ENTER

PRINT CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

6.Edit Cashier

NO DATA

CASHIER # 1

SASHA

Not Found in DB

Create?

CAHSIER #     7

PRINT CHANGES?

ENTER=Yes, ESC=No

EDIT MENU

6.Edit Cashier

CASHIER # 1

SASHA

CASHIER # 4

FRAM

CASHIER # 4

FRAM

PRINT CHANGES?

ENTER=Yes, ESC=No

READY

12/05/05      10:03 PM

ECR MAIN MENU

3.Merch. Options

MERCH. OPTIONS

6.Tax Menu

TAX MENU

1.Set Tax %

Tax 1 %

5.5000

READY

12/05/05      10:03 PM

ECR MAIN MENU

3.Merch. Options

MERCH. OPTIONS

6.Tax Menu

TAX MENU

2.Tax Name

Tax 1    Change ?

ENTR-Yes, ESC-No

ENTER TAX NAME

READY

12/05/05      10:03 PM

ECR MAIN MENU

4.System Options

SYSTEM OPTIONS:

1.Set Time/Date

12/05/2005

13:24:00

SETTING DATE:

MM/DD/YY

SETTING TIME:

hh:mm:00

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

4.System Options

SYSTEM OPTIONS

2.Site ID

CHANGE SITE ID ?

1234567

Manager Card or

ESC for Password

Swipe Man. Card

or Enter Site ID

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

4.System Options

SYSTEM OPTIONS:

3.Reset Database

Manager Card or

ESC for Password

ARE YOU SURE?

ENTER=Yes, ESC=No

CHANGE SITE ID ?

2292491

ECR CLOSED

12/05/05      10:03 PM

ECR MAIN MENU

5.BarCode Functs

BarCode Function

1.Print BarCode

AVAILABLE TYPES

1.EAN-13

ENTER CODE

ENTER CODE

1234567890123

READY

12/05/05      10:03 PM

ECR MAIN MENU

6.POS Comm.

Comm. Options

1.Line Params

Line Params

1.Max Retries

Max Retries

READY

12/05/05      10:03

ECR MAIN MENU

6.POS Comm.

Comm. Options

1.Line Params

Line Params

2.Dial Type

Dial Type

1.Tone

READY

12/05/05      10:03

ECR MAIN MENU

6.POS Comm.

Comm. Options

1.Line Params

Line Params

3.Dialing Prefix

Dialing Prefix

READY

12/05/05      10:03

ECR MAIN MENU

6.POS Comm.

Comm. Options

1.Line Params

Line Params

4.Phone# Display

Phone# Display

1.Yes

READY

12/05/05      10:03

ECR MAIN MENU

6.POS Comm.

Comm. Options

1.Line Params

Line Params

5.Break Mode

Break Mode

1.ON

READY

12/05/05      10:03

ECR MAIN MENU

8.POS Reports

ENTER PASSWORD

REPORTS:

1.Default Report

REPORTS:

2.Current Report

CUR. REPORT TYPE:

1.Condensed Rprt

CHOOSE EDC TYPE:

1.ALL

ENTER CARD TYPE:

1.ALL

SORT METHOD:

1.By Trans #

CHOOSE TRAN. TYPE

1.ALL

Set Cur. Defaults

NO                YES

REPORTS:

3.History Report

From Batch Date:

11/01/05

To Batch Date:

11/30/05

HISTORY REPORTS

1.Total

CHOOSE EDC TYPE

1.ALL

ENTER CARD TYPE

1.ALL

CHOOSE TRAN.  TYPE

1.ALL

REPORTS:

6.Performance

CHOOSE EDC TYPE

2.CREDIT

Reset Perf Rprt?

NO                     YES

REPORTS:

8.Report Setup

Report Setup:

1.Vis/Mastr Setp

Vis/Mastr Setup

1.Separately

6PK 12OZ WATER

Exc123                   4.99

50.00

DEPARTMENT #

DEPARTMENT #

98

Prepaid Phone

Exc123                  50.00

CHOOSE TENDER

112.34

Start of

PHONE CARD Auth

PREPAID

PASSWORD     --->

Select:

1.PIN Sale

Enter PIN Code:

Enter amount:

0.00

DEPARTMENT #

50.00

6PK 12OZ WATER

Exc123                   4.99

DEPARTMENT #

98

Prepaid Phone

Exc123                  50.00

CHOOSE TENDER

112.34

Start of

PHONE CARD Auth

PREPAID

PASSWORD     --->

Select:

2.Card TopUp

Swipe Card or

Enter Account:

Enter amount:

0.00

Transaction Type:

1.Credit

6PK 12OZ WATER

Exc123                   4.99

52.70

DEPARTMENT #

DEPARTMENT #

98

Prepaid Phone

Exc23                    52.70

CHOOSE TENDER

112.34

Start of

PHONE CARD Auth

PREPAID

PASSWORD     --->

Select:

3.Bill Payment

Payee ID:

Account Number:

Enter amount:

0.00

Confirm Account:

CHANGE SITE ID ?

2292491

ECR CLOSED

12/05/05      08:50AM

PC COMMUNICATION

1.Auto Load

PC COMMUNICATION

PROCESSING . . .

ECR CLOSED

12/05/05      08:52AM

DIALING

18005551234

New Journal #

DIALING

18005551234

See next page for explanations.

Ntx means that the item is not taxable.

txExc3 means that the item is exempt from tax #3 only.

Manager Card or

ESC for Password

TEAR SLIP   ---->

Press any Key . . .

DISCOUNT %

0.00

DISCOUNT $

0.00

KEY IN AMOUNT

0.00

VOID

VOID TRANS #

VERIFY

CREDIT . . . . VERIFY

ACCOUNT       -->

1-DSCNT IN %

2-DSCNT IN $

DISCOUNT $

0.00

DISCOUNT %

0.00

Press any key . . .

COUNTING DATA

PLEASE WAIT . . .

1-By Code

2-By Dept. #

FROM PLU *

DEPARTMENT #

ECR MAIN MENU

3.Merch. Options

MERCH. OPTIONS

1.Operation Mode

Operation Mode

1.Nurit WEB

DEPARTMENT # 4

PRODUCE

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

2.Trans Upload

PC COMUNICATION

PROCESING . . .

PC COMUNICATION

PROCESING . . .

PC COMMUNICATION

3.PLU Download

ECR CLOSED

12/05/05      10:03 PM

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

1.Batch to Host

DIALING

CHOOSE HOST:

1.ALL

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

4.Dept. Download

PC COMUNICATION

PROCESING . . .

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

5.Cashier Dwnld

PC COMUNICATION

PROCESING . . .

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

6.Client Dwnld

PC COMUNICATION

PROCESING . . .

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

7.Auto Load

PC COMUNICATION

PROCESING . . .

ECR CLOSED

12/05/05      10:03 PM

PC COMMUNICATION

8.Employee Rpt

PC COMUNICATION

PROCESING . . .