Survey Manual

Chapter 8

Resources

Colorado Department of Transportation

October, 2003

TABLE OF CONTENTS

Chapter 8 – Resources

8.1	General	3

8.2	Resources	4

8.2.1	Simple Curve	4

8.2.2	Simple Curve Computations	5

8.2.3	Simple Curve Computations	6

8.2.4	Vertical Curve	9

8.2.5	Spiral Curve	11

8.2.6	Compound Curve	17

8.2.7	Reverse Curve	18

8.2.8	Short Radius Curve	19

8.2.9	Deflections for Spiral Transition Between Simple Curves	20

8.2.10	Inaccessible PI Procedure	21

8.2.11	Alignment & Curve Abbreviations & Symbols	22

8.2.12	Area Calculations of Earthwork by Double Meridian Distance	24

8.2.13	Earthwork Volume Calculations by Average End Area	28

8.2.14	Area of Plane Figures	30

8.2.15	Volume and Surface Areas of Solids	34

8.2.16	Abbreviations	38

8.2.17	Weights, Measures & Equivalents	45

8.2.18	Glossary	49

8.2.19	Conversion Tables	53

8.2.20	Temperature Correction Table Chaining	54

8.2.21	Trigonometric Formulas & Functions	55

8.2.22	Computation of Unknown Bearings	56

8.2.23	Standard Arm Signals	57

8.3	References	59

## General

The purpose of this chapter is to provide the surveyor with an easy to use resource of information that will enable the user of this manual to reduce her/his library of reference material needed in the field.

This chapter is not intended as a textbook on surveying, rather it provides a reference source for formulas, tables and information. No representation is made or warranty given as to its content. User assumes all risk of use. CDOT assumes no responsibility for any loss or delay resulting from such use.

## Resources

### Simple Curve

### Simple Curve Computations

### Simple Curve Computations

### Vertical Curve

### Spiral Curve

(SPIRAL CURVE EXAMPLE CONTINUED)

Compute Simple Curve Deflection as shown in “Example for Simple Curves”

Station				Deflection

S.T.	692+48.26			0’00’00”

692+00				0’04’16”

691+50				0’17’42”

691+00				0’40’18”

690+50				1’12’04”

690+00				0’53’00”

689+50				2’43’05”

C.S.	689+48.26			2’45’00”

### Compound Curve

### Reverse Curve

### Short Radius Curve

### Deflections for Spiral Transition Between Simple Curves

### Inaccessible PI Procedure

### Alignment & Curve Abbreviations & Symbols

ALIGNMENT & CURVE

ABBREVIATIONS & SYMBOLS

C.S.			Point of change from circular curve to spiral.

d				(For Simple and Spiral Curves) Deflection angle. Intersection angle formed by a tangent and a chord. (For Vertical Curves) The tangent offset from the grade line to a point on the curve.

(For Inaccessible P.I. Procedure) Distance from the midpoint of the long chord to the P.I.

Dc				Degree of circular curve.

Es				External distance, P.I. to center of circular curve.

K				Distance from T.S. to point tangent opposite the P.C. of the circular

curve produced.

I				Length between T.S. and S.T. and any other point on the spiral.

L.C.			Straight line chord distance between T.S. & S.C. (long chord).

Ls				Length of spiral between T.S. & S.C.

L.T.			Long tangent distance of spiral only

P				Offset distance from the tangent of P.C. of circular curve produced.

P.C.			Point of change from tangent to circular curve.

P.C.C.		Point of compound curve.

P.I.			Point of intersection of the main tangents.

P.O.C		Point on a circular curve.

P.O.S.		Point on  a spiral curve

P.O.S.T.		Point on a semi-tangent.

P.O.T.		Point on a tangent

P.R.C.		Point on reverse curve.

P.T.			Point of change from circular curve to tangent.

S.C.			Point of change from spiral to circular curve.

ALIGNMENT & CURVE

ABBREVIATIONS & SYMBOLS

### Area Calculations of Earthwork by Double Meridian Distance

### Earthwork Volume Calculations by Average End Area

### Area of Plane Figures

### Volume and Surface Areas of Solids

### Abbreviations

A						A

ABC					aggregate base course

Abn					abandon

Abut					abutment

Adj					adjusted

AC					asphalt cement

Ah					ahead

AHW				allowable headwater

Alt					alternate

Approx				approximate

Asph					asphalt

Assy					assembly

Att					attenuator

Ave					avenue

Avg					average

@						at

B						B

BCR					begin curb return

Beg					begin

Bit Ctd				bituminous coated

Bit SL				bituminous seal

Bit Surf				bituminous surfacing

Bk						back

Bkf					backfill

BL					base line

Bldg					building

Blvd					boulevard

BM					bench mark

Bot					bottom

Br						bridge

BS					backsight

BT					beginning of transition

BW					barbed wire

C						C

C						cut

CAA					cable anchor assembly

Calc					calculated

CAP					corrugated aluminum pipe

CBC					concrete box culvert

CCS					Colorado Coordinate System

CDOH				Colorado Department of Highways

CF or Cu.Ft		cubic feet (foot)

C & G				curb and gutter

Chnl					channel

Cl						class

CL					chain link

Chainman

CL						centerline or control line

Clr					clear, clearance

Co						county

Conc					concrete

Cond					conduit

Conn					connector

Const					construction

Cont					continued

Coord				coordinate

CPS					concrete pipe sewer

Cr						creek

CSP					corrugated steel pipe

CSPA				corrugated steel pipe arch

CSPS      			corrugated steel pipe sewer

CTB					cement treated base

Culv					culvert

CY or Cu.Yd.		cubic yard(s)

D						D

Dbl					double

Def					deflection

Deg					degree

Del					delineator

Det					detour

DHW				design headwater

Dl						drop inlet

Dia or  (				diameter

Dim					dimension

Dist					distance or district

Dr						drive

Dwy					driveway

E						E

E						east

Ea						each

Easmt				easement

ECR					end curb return

EDM					electronic distance meter

Elev					elevation

Emb					embankment

EO					edge of oil

EP						edge of pavement

Eq						equation

ES						edge of shoulder

ET					end of transition

ETW					edge of traveled way

Exc					excavation

Exist					existing

F						F

F						fill

Fdn					foundation

Fe						fence

FH					fire hydrant

Flr						flare

FL or FL 			low line

FP						fence post

FR					frontage road

FS						foresight

Ft						foot (feet)

Ftg					footing

Fwy					freeway

F & C 				frame and cover

F & G				frame and grate

FG					finish grade

G						G

G						gutter

Ga						gauge, gage

Galv					galvanized

GL					gas line

GM					guard marker

GR					guard rail

GSP					galvanized steel pipe

GV					gas valve

H						H

H						height

HBP					hot bituminous pavement

Hdwl					headwall

Hl						height of instrument

Horiz					horizontal

HP					hinge point

Hwy					highway

H & T				hub and tack

I						I

IB						imported borrow

In						inch

Inst. Or 				instrument or instrument man

Int						intersection

Intch					interchange

Inv					invert

Irr						irrigation

J						J

K						K

L		 				L

Ln						lane

L						length

LF or Lin.Ft.		linear feet (foot)

Loc					location

Lt						left

M						M

Matl					material

Max					maximum

MB					mail box

MDS					maximum design speed

Med					median

MES					metal end section

MH					manhole

Mi						mile(s)

Min					minimum

Misc					miscellaneous

Mkr					marker

Mod					modified or modify

Mon					monument

MP					mile post(s)

MPH					miles per hour

MS					minor structure

N						N

N						north

NGS					National Geodetic Survey

No. or #				number

(						note keeper

O						O

Oblr					obliterate

OG					original ground

OH					overhead

O/S					offset

P						P

P						page

PB					pull box

PC					party chief

PCSP					perforated corrugated steel pipe

P & Abn				plug and abandon

Ped					pedestrian

PGL					profile grade line

PK Nail				Parker-Kalon nail

PL						property line

PMBB				plant mix bituminous base

PP						power pole

Proj.					projected, project

PSP					perforated steel pipe

PSS					point of slope selection

Pt						point

Pvmt					pavement

PVPP				polyvinyl plastic pipe

Q						Q

Q						volumetric flow rate

R						R

R						radius

RCP					reinforced concrete pipe

RCPA				reinforced concrete pipe arch

RD					road

Rdwy					roadway

RE					Resident Engineer

Reinf					reinforced

Rel					relocate

Riv					river

ROW 				right of way

RP					radius point or reference point

RR					railroad

Rt						right

Rte					route

RW					retaining wall

rod man

S						S

S						south

Salv					salvage

San.Swr.			sanitary sewer

SB Fe				sound barrier fence

SD					storm drain

Sec					section

SES					steel end section

SF or Sq. Ft.		square foot (feet)

SG					sub grade

Shld					shoulder

Sht					sheet

SL						survey line

Sl Coat				seal coat

Spec					special, specification

Sp						spillway

SS						slope stake

Sta					station

Std					standard

St						street

Stm Swr				storm sewer

Str						structure

Surf					surfacing

SW					sidewalk

Swr					sewer

SY or Sq. Yd.		Square yard(s)

T						T

Tan					tangent

Tbr					timber

TCB					traffic control box

Temp					temporary

TP						turning point

Trans					transition

Trav					traverse

TT					transmission tower

TY					type

Typ					typical

Typ.Sec. 			typical section

U						U

UD					under drain

USGS				United States Geological Survey

V						V

V						valve

Var					variable

VC					vertical curve

VCP					vitrified clay pipe

Vel					velocity

Vert					vertical

VP					vent pipe

W						W

W						West

WH					weep hole

WL					work line

WM					wire mesh

WSP					welded steel pipe

WV					wing wall

X						X

Xing					crossing

X-Sec				cross section

Y						Y

Z						Z

### Weights, Measures & Equivalents

WEIGHTS, MEASURES & EQUIVALENTS

Acre=								43560 square feet

4840 square yards

160 square yards

4047 square meters

.4047 hectares

10 square chains

Acre Foot=							43560 cubic feet

325,829 gallons

Acre=								100 square meters

Barrel of Cement=				376 pounds

Celsius=								(C x 9/5) +32 Fahrenheit

oC + 273.18 Kelvin

Centimeter=						.03937 inches

.01 meters

Centimeter of Mercury=		.1934 pound/square inch

Chain=								792 inches

(surveyor’s)						20.12 meters

66 feet

4 rods

22 yards

100 links

Circumference of Circle=		2 ( R

Cubic Centimeter=				3.531 x 10–5

.06102 cubic inches

1 X 10–6 cubic meters

2.642 x 10–4 gallons

Cubic Foot=						28,320 cubic centimeters

1728 cubic inches

.02832 cubic meters

.03704 cubic yards

7.48052 gallons

62.4 pounds of water

Cubic Foot/Second=				0.646317 million gallons/day

.0005787 cubic feet

Cubic Meter=						1 x 106 cubic centimeters

35.31 cubic feet

1.308 cubic yards

264.2 gallons

Cubic Yard=						27 cubic feet

0.7646 cubic meters

202 gallons

46,656 cubic inches

Degree=								.0174533 radians

60 minutes

3600 seconds

Fahrenheit (degree)=				(F –32) 5/9 Celsius

(F –32) 5/9 + 273.18 Kelvin

Foot (U.S. Survey)=				1200/3937= 0.30480061 meters

304.80061 millimeters

30.480061 centimeters

Foot (International)=				0.3048 meters

3048 millimeters

30.48 centimeters

Foot of Water=					43.35 pounds/square inch

Foot/Second=						.06818 miles/hour

1.097 kilometers/hour

Gallon=								3,785 cubic centimeters

.1337 cubic feet

231 cubic inches

3.785 liters

8.337 pounds of water

Gallon/Minute=					.002228 cubic feet/second

Gram=								.002205 pounds

.001 kilograms

.03527 ounces

Hectare=							2.471 acres

100 acres

10,000 square meters

Inch=									2.54 centimeters

.08333 feet

Inch of Mercury=					.4912 pounds/square inch

Kilogram=							2.2046 pounds

35.274 ounces

Kilometer=							1 x 103 meters

3281 feet

Link=								7.92 inches

.66 feet

1/100 chain

Liter=								1 x 103 cubic centimeters

.03531 cubic feet

61.02 cubic inches

.2642 gallons

Meter=								100 centimeters

3.2808 feet

39.37 inches

.001 kilometers

.0006214 miles

1.094 yards

Mile=								5280 feet

63360 inches

1760 yards

1609 meters

Mile/Hour=							1.467 feet/second

1.6093 kilometers/hour

Mil=									.001 inches

Minute=								.01667 degrees

60 seconds

Ounce=								28.35 grams

.0625 pounds

Ounce (fluid)=						1.805 cubic inches

.02957 liters

.0078 gallons

Pound=								453.59 grams

.0005 tons

16 ounces

Pound of Water=					27.68 cubic inches

.1198 gallons

Pound/Square Inch=				2.036 inches of mercury

Quart=								.25 gallons

.9463 liters

Radian=								57.296 degrees

Rods=								5.5 yards

16.5 feet

.003125 miles

Seconds=							.0003778 degrees

.01667 minutes

Square Centimeter=				.001076 square feet

.155 square inches

.0001 square meters

Square Feet=						.1111 square yards

.0929 square meters

144 square inches

Square Inch=						.006944 square feet

6.452 square centimeters

Square Meter=						.0002471 acres

10.76 square feet

1.196 square yards

Square Mile=						640 acres

2.59 x 106 square meters

Square Yard=						.0002066 acres

9 square feet

1296 square inches

.8361 square meters

Ton=									2000 pounds

907.18 kilograms

Yard=								3 feet

.9144 meters

36 inches

.0005682 miles

### Glossary

GLOSSARY

Alignment-					A formation of points, lines, angles, and curves showing the direction and components of the centerline.

Backsight-					The transit or level sight back on survey line. (Stationing decreases back.)

Bench Marks-				A semi-permanent or permanent physical mark or object of known elevation.

Blue Tops-					Grade stakes marked with blue keel, whiskers, or paint denoting top of sub grade.

Blunders-					An unpredictable human mistake.

Centerline or

Control line-				The line midway between the sidelines of an alignment, to which the survey is tied.

Chain-

(Engineers)					A steel tape, 100 feet in length. The last foot on each end of the tape is divided in tenths of foot. The last tenth is usually calibrated in hundredths of a foot.

Control Monuments

(Primary)-					CDOT Type 2 monuments established on the ground as the framework for the Primary Control Survey Network. This includes the existing control monuments used as reference for the establishment of the primary control network, and is used to control all horizontal and vertical components of the survey.

Control Monuments

(Secondary)-				Monuments established from the approved Primary Control Monuments. The secondary control monuments are typically established as survey work points in areas that require additional control be set at a lesser accuracy than that of the Primary Control Network.

Control Network

(Primary)-					A network of Primary Control Monuments permanently monumented on the ground as the framework for the Primary Control Survey.

Control Points-			Points on an alignment which are necessary to re-establish the alignment.

Control Survey

(Primary)-					The survey performed to obtain the final horizontal and vertical data for the Primary Control Monuments used to control all horizontal and vertical components of the survey and any future surveys in and along the highway corridor.

Corner, Lost-				When the original corner cannot be determined beyond reasonable doubt, it is a lost corner.

Corner, Meander-			A corner placed at the mean high water mark on a surveyed line, where the body of water is greater than 3 chains in width on the surveyed line.

Corner, Obliterated-		If the monument or marker of the existing corner can not be found, it is obliterated, but not necessarily lost.

Cross Sections-			Profiles at the right angle to the centerline or control line of a survey showing all breaks in grade of the ground line to truly reflect the ground situation.

Differential

Leveling-					Used for setting bench marks by determining the differences of elevation between two points of which the first point’s elevation is known. Theory and application is expressed as:

Elev. A + B.S. = H.I.

H.I. – F.S. =Elev. B

Electronic Distance

Meter-						An instrument which uses microwaves, modulated light beams or laser light to measure distances.

Error-						The difference (after blunders have been eliminated) between a measured or calculated value of a quantity and the true or established value of the quantity.

Field Notes-				A permanent written or electronic record of the survey including all pertinent information, measurements, calculations and observations made during the course of the survey.

Foresight-					The transit or level sight ahead on survey line. Stationing increases ahead.

Guard-						A stake placed to protect a hub, marked with the information describing the point.

Hand Level-				A small hand instrument with a small bubble periscoped so that it shows in the field of view. The instrument is level when the reflected bubble is on the cross hair.

Height of instrument-	The known elevation of the instrument at the center of the telescope.

Hub-							A stake driven flush or even with the ground, denoting elevation and/or line.

Inverted Transit-			The transit with the telescope reversed and level bubble on top.

Level-						A precision instrument used to establish elevation. Consists of an adjustable telescope with horizontal and vertical cross hairs. A bubble and adjustable tangent screws level the instrument.

Level Rods-				Rod marked in feet, tenths of a foot and hundredths of a foot to be used  in conjunction with the level in establishing elevations and stadia.

Normal Transit-			Transit telescope in erect position,  level bubble below. Sometimes referred to as direct.

0+00-						Denotes the starting point or beginning of stationing. Any designation with 00 after it is a full, complete, or even station. Any designation after the + sign is a fraction of a station.

Plus Fifties-				(Half Station) The fifty foot interval between stations.

Pole, Range-				Also called range rod or picket.  A metal or wood pole with a steel point, usually banded in alternate red and white sections, one foot wide. Usually six to eight feet long, range rods are used to give sight to the transit man.

Profile Leveling-			Determining existing ground surface elevations along a definite line by means of a level and a direct reading rod. These elevations are then plotted to show a graphical representation of the intersection of a vertical surface. Usually a much larger vertical scale than horizontal scale is used to accentuate the differences of elevation.

Reference

Monuments-				When two or more monuments are established to accurately perpetuate the true monument they become reference monuments and are set as close as practicable to the true monument, and meet the same physical standards required to set the true monument. (See Witness Corner)

Reference Points-			A point that gives information so that another point can be re-established.

Right of Way-				Area of land required to construct a road.

Right of Way

Monument-					CDOT Type 1 monument established on the ground set to define the Departments land boundaries in the field.

Slope Stakes-				Stakes set to mark the outside limits of the grading operation giving information as to the construction of the road.

Station-						A full chain  or steel tape distance of 100 feet. Locations along the alignment are designated as stations. New stationing is consecutively numbered from West to East and from South to North.

Super elevation-			Adjusting the slope perpendicular to centerline for the purpose of counteracting centrifugal force.

Tangent-					The straight line of a survey.

Tangent of a Curve-		The distance from the P.I. to the P.C. and P.T. or T.S. and S.T.

Theodolite/ Transit-		Precision instruments used for the establishment and location of lines upon the earth’s surface. They consist of an adjustable telescope with horizontal and vertical cross hairs, stadia hairs and vertical and horizontal vernier plates for determining the angular measurements. The term “transit” is limited to an instrument which has open verniers that must be read directly with the naked eye or with the aid of a hand held magnifier. Theodolites have closed, optical reading verniers.

Topography-				A surveying process in which the positions with respect to the horizontal control line and description of the natural and artificial features of a given locality are obtained and recorded.

Turning Point-				A point used between bench marks as a temporary turning elevation.

Vernier-						A device used to obtain readings smaller than the smallest division on a scale.

Witness Monument-		When only one reference monument is established to perpetuate the location of the true monument, it becomes a witness monument and is to be set within 660 feet, preferably in one of the surveyed lines leading to the true monument location. However, the witness monument can be set in any direction within a distance of 330 feet. (See Reference Corner)

### Conversion Tables

### Temperature Correction Table Chaining

### Trigonometric Formulas & Functions

### Computation of Unknown Bearings

### Standard Arm Signals

## References

CDOT Survey Manual – CDOT, 1992

CDOT Survey Manual – CDOT, 1984

CDOT Survey Manual – CDOT, 1966

Memorandum of Understanding between the State Board of Registration for Professional Engineers and Land Surveyors and the Colorado Department of Transportation – July 1, 1985, Revised January 13, 1995.

Board of Registration for Professional Engineers and Land Surveyors, Land Surveying Laws and Board Rules – July, 2002

@ http://www.dora.state.co.us/engineers_surveyors/

Definitions of Surveying and Associated Terms – ACSM / ASCE, 1978 (rev), Reprinted 1984.

Second Edition Surveying with Construction Applications – by Barry F. Kavanagh

# Text boxes

Point of change from on spiral curve to the next spiral cure.

Point of change from spiral to tangent.

Tangent distance from P.I. to T.S. or S.T.

Point of change from tangent to spiral.

Coordinate of S.C. from T.S. or C.S. from S.T.

Angle.

Right Angle.

Intersection angle between tangents of entire curve.

Intersection angle between tangents at the S.C.  and at the C.S. or the central angle of circular curve portion of the curve.

Intersection angle between tangents of complete curve and tangent at any other point on the spiral.

Intersection angle between tangents of complete curve and tangent at the S.C.

Deflection angle from tangent at T.S. to S.C.