----------------------------------------------
               |                                              |
               |                                              |
               |                 G e o C a l c                |
               |                                              |
               |     C O o r d i n a t e   G e O m e t r y    |
               |                                              |
               |                  ( C O G O )                 |
               |                                              |
               |                 Version  1.22                |
               |                                              |
               |                                              |
                ----------------------------------------------




                                   SURVEYING

                                       &

                                  ENGINEERING

                             APPLICATIONS SOFTWARE










                     Program Operations & Reference Manual















                              All Rights Reserved
          Copyright (c) 1986, 1987 GeoCalc Software Systems Co., Inc.
                                 P.O. Box 5308
                            Philadelphia, PA 19142
                                (215) 365-5585






                                                              Page   2

                                 TABLE OF CONTENTS

         Table of Contents........................................  2
         Introduction.............................................  5
         User-Supported Software..................................  6
         Registration.............................................  8
         Invoice Form.............................................  9
         Copyright Notice, Disclaimer, & Tradenames............... 10
         System Requirements & File Listings...................... 11
         Backing Up The Disks..................................... 13
         Configuring The COGO Program............................. 14
         A History of COGO........................................ 15
         Terminology, Application Techniques...................... 17
         Booting The COGO Program................................. 18
         Plotting (CADD), HP-11C Emulator, Exclusion.............. 19
         General File Structure................................... 20
              Specifying & Using Figures.......................... 21
              Curve Definitions Within Figures.................... 22
         Command List............................................. 23
         Overview of Version 1.22................................. 24
              On-line Help........................................ 25
              RAM Resident Utilities.............................. 26
              Input............................................... 27
              Missing Data........................................ 27
              Comments............................................ 27
              Abbreviations....................................... 27
              Command Codes....................................... 27
              Precision........................................... 27
              Stationing.......................................... 28
              Output.............................................. 28
              DMS Format.......................................... 28
              Bearings............................................ 28
              Quadrant Codes...................................... 28
              Azimuths............................................ 28
              Direction Sign...................................... 28
              Angular Expressions................................. 28
              Angular Delimiters.................................. 29
              Distance Delimiter.................................. 29
              Repeatability....................................... 29
              Delimiter Summary................................... 29
              Angular/Distance Input Examples..................... 30
              Figures & Figure Transpositions..................... 31
              Caps Lock........................................... 31
              Coordinate/Figure Areas............................. 31
              The "Flip Up" Menu.................................. 32
              The "Flip Up" Inch/Foot Conversion Table............ 32
         Control Commands......................................... 33
              File Maintenance Commands........................... 33
              Points Maintenance Commands......................... 33
              Figure Maintenance Commands......................... 34
              Line & Curve Extension Commands..................... 34
              Points Move Commands................................ 34
              Points Definition Commands.......................... 35
              Line & Curve Intersection Commands.................. 35




          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   3

                                 TABLE OF CONTENTS


        Control Commands (continued)
              Data Display Commands............................... 36
              Figure Alignment Commands........................... 36
              Spiral Commands..................................... 37
              Alignment Commands.................................. 37
         Command Variable Names................................... 38
         Adjust Area.............................................. 39
         Alignment................................................ 40
         Alignment Offset......................................... 41
         Angles................................................... 42
         Arc Arc Intersect (Dist/Dist Intersect).................. 43
         Arc Line Azimuth  (Az/Dist Intersect).................... 44
         Arc Line Bearing  (Brg/Dist Intersect)................... 45
         Arc Line Points.......................................... 46
         Area..................................................... 47
         Area Azimuth............................................. 48
         Area Bearing............................................. 49
         Azimuth Intersect (Az/Az Intersect)...................... 50
         Batch Print.............................................. 51
         Batch Screen............................................. 52
         Bearing Intersect (Brg/Brg Intersect).................... 53
         Compound Spiral.......................................... 54
         Convert Meridian......................................... 55
         Coordinate Offset........................................ 56
         Coordinate Point on Arc.................................. 57
         Coordinate Point on Spiral............................... 58
         Copy File................................................ 59
         Curve Spiral............................................. 60
         Define Curve............................................. 61
         Delete Coordinates....................................... 62
         Delete Figures........................................... 63
         Describe Alignment Azimuth............................... 64
         Describe Alignment Bearing............................... 65
         Distance................................................. 66
         Divide Arc............................................... 67
         Divide Figure............................................ 68
         Divide Line.............................................. 69
         End Of Job............................................... 70
         End Of Run............................................... 71
         Extend Arc............................................... 72
         Figure Arc Intersect..................................... 73
         Figure Figure Intersect.................................. 74
         Figure Line Intersect.................................... 75
         Fit Alignment............................................ 76
         Fit Curve................................................ 77
         Get Coordinates.......................................... 78
         Get Figures.............................................. 79
         Inverse Azimuth.......................................... 80
         Inverse Bearing.......................................... 81






          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   4

                                 TABLE OF CONTENTS


         Line Spiral.............................................. 82
         List Coordinates......................................... 83
         List Figures............................................. 84
         List Files............................................... 85
         Locate Angle............................................. 86
         Locate Azimuth........................................... 87
         Locate Bearing........................................... 88
         Locate Deflection........................................ 89
         Locate From Alignment.................................... 90
         Locate Line.............................................. 91
         Offset Alignment......................................... 92
         Parallel Figure.......................................... 93
         Parallel Line............................................ 94
         Points Azimuth Intersect................................. 95
         Points Bearing Intersect................................. 96
         Points Intersect......................................... 97
         Points On Alignment...................................... 98
         Redefine................................................. 99
         Segment..................................................100
         Segment Plus.............................................101
         Segment Minus............................................102
         Simple Curve.............................................103
         Simple Spiral............................................104
         Spiral Length............................................105
         Spiral Offset............................................106
         Spiral Spiral............................................107
         Start Of Job.............................................108
         Station And Offsets......................................109
         Stations From Coordinates................................110
         Store....................................................111
         Store Figure.............................................112
         Store Job................................................113
         Streets Intersect........................................114
         Tangent..................................................115
         Tangent Offset...........................................116
         Traverse Angles..........................................117
         Traverse Azimuths........................................118
         Traverse Bearings........................................119
         Traverse Deflections.....................................120
         Type Print...............................................121
         Type Screen..............................................122
         Error List Summary.......................................123
         A Sample Session (interactive)...........................127
         A Sample Session (batch).................................132
              A "PROper" BATCH Example............................134
              A "COMmon" BATCH Example............................135
         Bug Report...............................................136
         Comment/Suggestion Report................................137
         Acknowledgements.........................................138
         Future Versions..........................................139
         Chronology...............................................140




          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   5

                                 INTRODUCTION


         Welcome to GeoCalc Software System's COordinate GeOmetry
         (COGO) Surveying/Engineering applications program.  We hope
         that your evaluation finds this software capable and
         efficient, and your use of it enjoyable and profitable.

         If you are a first-time user of this type of "command
         oriented" COGO, you will find it easy to use and learn right
         from the very beginning (please read this documentation,
         though).  If you are an old hand at COGO, you will find it
         quite powerful to use while also offering some subtle (and
         not so subtle) amenities that we hope will increase both your
         speed of data entry and your overall satisfaction with the
         program.

         We at GeoCalc are land surveyors with many years of
         experience in engineering, rural, urban, control surveys and
         design work.  We are also hackers of some renown (if we do
         say so ourselves), who have used mainframe COGO for many
         years.  This has provided our design and programming team the
         necessary and valuable experience in formulating the
         groundwork for what was to become GeoCalc's COGO.

         For those users who are new to this particular type of COGO
         input/output format, we believe you will be treated to a
         most productive encounter.  We strongly suggest that you
         power up the program and run COGO at every opportunity; you
         will find that you attain the highest degree of efficiency
         when the majority of commands become relatively familiar.
         Once familiarity is attained, you can concentrate on
         "tactics" and the myriad shortcuts that are helpful when
         solving systems of figures in a complex geometric project.

         We have placed this software into the "Public Domain"
         distribution network (as SHAREWARE - see following pages)
         with the recognition that we must maintain our support,
         maintenance, and update obligations to the surveying,
         engineering, and educational communities.  With your
         assistance, we will fulfill those obligations.

















          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   6

                            USER SUPPORTED SOFTWARE


         P L E A S E   C O P Y   &   R E D I S T R I B U T E   T H I S
         ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
                             S O F T W A R E ! ! !
                             ~~~~~~~~~~~~~~~~~~~~~

         To avoid the costs of standard commercial marketing methods
         (and the necessity of having to pass those costs on to our
         customers), we have chosen to offer our COGO via the public
         domain distribution network as "USER SUPPORTED SOFTWARE".
         This unique marketing method has been in use and successful
         for many popular software products.  For example, the
         "PC-Write" word processing system has been distributed using
         the concept of "SHAREWARE" by Mr. Bob Wallace of QUICKSOFT
         who previously designed and wrote a large part of MS-PASCAL.
         The late Andrew Fluegelman of the HEADLANDS PRESS and one of
         the founding editors of PC World magazine, marketed the
         "PC-Talk III" communications package (a virtual standard)
         using his "FREEWARE" concept.  "PC-File III" is an extremely
         popular data base management system written by Mr. Jim Button
         of BUTTONWARE and marketed under the "USER SUPPORTED" method.
         GeoCalc's COGO is being marketed in the same fashion and can
         be obtained through the various means of communication open
         to all computer users: Bulletin Boards, User's Groups,
         Computer Clubs, Professional Societies and Organizations,
         etc.  If these sources of distribution are not available to
         you, you can get a copy of GeoCalc's COGO by sending a
         formatted, double-sided disk (DOS 2.0+ only), a check for
         $10.00 to cover handling costs, and a stamped, self-addressed
         envelope to GeoCalc Software.  Please use a high quality 8
         1/2" x 11" envelope and include 2 stiff pieces of cardboard
         so the disk won't be bent in the mail.  GeoCalc will send
         its Ver. 1.22 COGO for your use and on-the-job evaluation.

         The USER SUPPORTED philosophy dictates that the usefulness
         and quality of software is best decided by the ultimate user,
         in a working environment, and at a pace which will allow a
         thorough evaluation of the product while under no pressure to
         purchase; and, that copying and unrestricted redistribution
         should be promoted and encouraged rather than prohibited by
         awkward, costly, inconvenient, and sometimes dangerous
         software and hardware protection schemes.  The methodology of
         distribution requires only that those who may have need of
         the particular software have free access to it; in turn, they
         should redistribute it to their friends and associates in the
         same unaltered form in which they received it and all users
         should register that software if it is useful to them.

         To paraphrase Mr. Fluegelman, the user supported concept is
         an experiment in economics, not altruism; it provides quality
         software without the author/distributor having to finance the
         marketing, distribution, advertising, and copy protection
         schemes that have become an expensive liability, while still
         allowing the author/distributor to be supported by sales of
         the software.

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   7

                            USER SUPPORTED SOFTWARE

         There are many excellent software packages marketed under the
         user supported method and all have one thing in common: they
         are willing to stand up to rigorous evaluation and testing
         before a purchase is made.  Those that are flawed, badly or
         unprofessionally written, buggy, or just not what is
         generally accepted as useful will fail and disappear.  Those
         that are effective, professionally written, and perform as
         advertised will succeed - thereby providing you with quality
         software at reasonable cost.  By registering user supported
         software, you will also be advocating the distribution of
         professional applications software that doesn't require you
         to sacrifice a year's net profits in order to finance its
         purchase.  Paying artificially high fees for software that
         accomplishes its task is bad enough, but paying hundreds or
         thousands of dollars for software that is not what you want
         is counterproductive.  It also encourages all those in the
         distribution chain to maintain or inflate prices.  The user
         supported method, on the other hand, allows the software
         designers (us) to bypass the advertising jungle (which is
         obscenely expensive), middle-men and distributors, and retail
         outlets (who often refer you to the technical or design types
         when you have a problem, anyway).  The software thus gets to
         you at a price that more closely reflects the true costs of
         development and a fair profit (you do not pay excessive
         profits or unnecessary overhead costs).

         YOU ARE ENCOURAGED TO COPY AND DISTRIBUTE GEOCALC'S COGO TO
         YOUR FRIENDS AND ASSOCIATES.  However, for the protection of
         everyone, certain distribution restrictions must apply:

              1) No compensation of any kind is to be charged for
                 the software  (exclusive of the diskette).
              2) Copyright or trademark notices, the name GeoCalc
                 Software Systems  Co., Inc., or the names of the
                 authors may not be removed or changed.
              3) The software  may not be altered  in any manner,
                 nor may  it be  redistributed  in any form other
                 than originally distributed by  GeoCalc Software
                 Systems.
              4) The software may not be distributed with or used
                 as an inducement to purchase any other software.

         The above restrictions are for the protection of all
         potential users of the program.  Please be particularly
         cognizant of item #3.  This will guarantee that you will
         receive all of the original software files.  If you should
         happen to receive the package from a friend who altered it,
         for example, than GeoCalc Software Systems could not answer
         any questions regarding it nor support it in any way.  If you
         should find the program not to your liking, PLEASE let us
         know why, and we will investigate and correct it if
         necessary.  But please do pass the program to others who may
         find it just what they need; your particular complaint may
         not be of concern to another user.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   8

                           REGISTRATION & LICENSING


         *************************************************************
         *                                                           *
         *                                                           *
         *       YOU MAY REGISTER GEOCALC'S COGO FOR A FEE OF        *
         *                                                           *
         *           | |                                             *
         *          *****     ******     *****      *****            *
         *         * | | *         *    *     *    *     *           *
         *         * | |           *    *     *    *     *           *
         *          *****      *****     ******     ******           *
         *           | | *         *          *          *           *
         *         * | | *         *          *          *           *
         *          *****     ******      ****       ****            *
         *           | |                                             *
         *                                                           *
         *                                                           *
         *************************************************************


         Your registration fee entitles you to direct telephone and
         mail support, and notification of future releases.  You will
         also immediately be sent the latest release which supports
         expanded coordinate point and figure storage, figure
         balancing, and DOS commands, and also includes a flip-up
         RAM-resident on-screen HP-11C calculator emulator, an on-line
         help system to interactively display command descriptions
         during COGO usage, and a complete CADD system.

         The staff at GeoCalc will be more than glad to answer any
         questions; a telephone is maintained to provide technical
         assistance for registered users.  Non-technical assistance
         will be provided to registered and non-registered users
         alike, and comments and suggestions are welcome and
         solicited.  Your critique is extremely important to us and
         all recommendations and requests will be seriously considered
         for implementation.  It is the intent of GeoCalc Software
         Systems to upgrade and amend COGO to reflect the needs and
         requests of the surveying and engineering community.

         For those who require an invoice, please use the form of the
         next page.  Or, call us at 215-365-5585 with your Master
         Charge or Visa number.  Registration fees are as follows:

                                      -PACKAGE-  -COGO ONLY-
         1) Registration of 1st copy   $399.00     $299.00
         2) Copy # 2 to copy #10 is    $369.00     $269.00
         3) Copy #11 to copy #20 is    $339.00     $239.00
         4) Over 20 copies                   A steal!

         For unique or unusual circumstances, or site licensing,
         GeoCalc Software Systems will be more than glad to work with
         any firm to help solve your particular requirements.
         Additional discounts of 16% will be allowed for bulk
         purchases (over 10 copies) by educational institutions.

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page   9

                                    INVOICE
                                    +++++++



         Pay:   GeoCalc Software Systems         Date: ____________
                     P.O. Box 5308
                 Philadelphia, PA 19142           No.: ____________
                      215-365-5585


         Sold To:    ______________________________________________

                     ______________________________________________

                     ______________________________________________

                     ______________________________________________



         Ship To:    ______________________________________________

                     ______________________________________________

                     ______________________________________________

                     ______________________________________________



          Quantity   Description               Unit Cost    Total
         ---------- ------------------------- ----------- -----------
                   | Registration of         |           |
                   | COGO V 1.22 - only!     |           |
                   | (Includes latest)       |           |
                   |  version)               |  $299.00  |
                   |                         |           |
                   | Registration of         |           |
                   | COGO V 1.22 (Includes:  |           |
                   | 11C Calc. Emulator &    |           |
                   | CADD System & latest    |           |
                   | version)                |  $399.00  |
                   |                         |           |
                   |                         |           |
                   |                         |           |
                   |                         |           |
         ---------- ------------------------- ----------- -----------
                                              Subtotal   = $
                    PA residents only add 6% sales tax   = $
                                                           ----------
                                                 Total   = $






          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  10

                             THE COPYRIGHT NOTICE


          This  Coordinate  Geometry  (COGO)  program  and   included
          documentation is  copyrighted (c)  1986 by GeoCalc Software
          Systems Company,  Inc.  of Philadelphia,  Pennsylvania  and
          Lawrence J. Cleary, PLS and  Raymond E. Havey, PLS, program
          authors.   Non-registered users  are hereby given a limited
          license to use this  product (Version 1.22)  for evaluation
          purposes only and to copy and re-distribute the program and
          its  accompanying  documentation  (known  as the  software)
          subject to the  following restrictions:

            1) No compensation of any kind is to be charged for
               the software (exclusive of the diskette).
            2) Copyright or trademark notices, the name GeoCalc
               Software Systems  Co., Inc., or the names of the
               authors may not be removed or changed.
            3) The software  may not be altered  in any manner,
               nor may  it be  redistributed  in any form other
               than originally distributed by GeoCalc Software.
            4) The software may not be distributed with or used
               as an inducement to purchase any other software.



                                THE DISCLAIMER


         In no event will the authors, distributors or re-distributors
         of GeoCalc's COGO,  or its  succeeding versions as originally
         distributed  by GeoCalc  Software Systems,  be liable for any
         damages,  including any lost  profits,  lost savings or other
         incidental or consequential damages arising out of the use of
         or inability to use the programs of COGO, even if the authors
         have been advised  of the possibility of such damages, or for
         any claim  by any  other party.   Users are  advised to  test
         GeoCalc's COGO thoroughly before relying on it,  as is common
         data processing procedure.   This software  is distributed on
         an "AS-IS" basis; use of the software  constitutes acceptance
         and  acknowledgement of the "AS-IS"  nature of  the software.



                     THE TRADE NAMES OR TRADEMARK CREDITS

         NAME           IS A REGISTERED TRADEMARK OR PROPRIETARY TO
         ~~~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         IBM            International Business Machines Corporation
         PC, XT, AT     International Business Machines Corporation
         Generic CADD   Generic Software Incorporated
         Sidekick       Borland International, Incorporated
         HP, HP-11C     Hewlett-Packard Company





          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  11

                              SYSTEM REQUIREMENTS

         GeoCalc's COGO is designed to be run on the IBM PC, PC-XT,
         PC-AT, and all close compatibles.

         The software requires:

              1) 640 Kb of RAM memory.
              2) A video display adapter conforming to the IBM Color
                 Graphics Adapter (CGA) or Enhanced Graphics
                 Adapter (EGA).
              3) A monochrome or color monitor.
              4) Two (2) disk drives (optionally, a hard disk).
              5) Optionally, a printer.

         Version 1.22 does not support a color screen display.

                              THE INCLUDED FILES

         Version 1.22 of GeoCalc's COordinate GeOmetry program MUST
         include all original files on the distribution diskette.  If
         any files are missing, please notify the source from which
         you obtained the program that it is incomplete, then contact
         GeoCalc Software Systems Co., Inc. to obtain the original
         distribution disk, as per the instructions on page 6.
         Ver. 1.22 consists of about a dozen programs and files that
         normally contain approximately 600Kb.  However, to make the
         distribution process less costly and inconvenient, the
         programs have been combined and squeezed by a compression
         utility (ARC.EXE) onto 1 diskette.  This utility will also
         allow you to unsqueeze and separate the programs into the
         format described on the next page.  As distributed on the
         squeezed/combined distribution diskette, the programs are as
         follows:

                    DISTRIBUTION DISK (Compressed/Squeezed)

         1) READTHIS.NOW          The text file that describes the
                                  unsqueeze process
         2) RUN.ARC               The squeezed COGO PROGRAM files
         3) DOC.ARC               The squeezed DOCUMENTATION files
         4) ARC.EXE               The utility program that unsqueezes
                                  all program/documentation files.


                From the DOS ready prompt A>, type the command:

                               TYPE READTHIS.NOW

         Instructions will scroll on your monitor that will describe
         how to unsqueeze/separate the archived (compressed) files
         onto two new diskettes.

         When the unsqueeze instructions are on your monitor screen,
         press the [SHIFT] and [PrtSc] keys simultaneously to dump the
         screen to your printer.  Now, perform the instructions.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  12

                              SYSTEM REQUIREMENTS


         Once the distribution diskette has been unsqueezed/separated,
         you will have 2 "original" diskettes with the following
         files:



                             COGO PROGRAM DISKETTE


         1) AUTOEXEC.BAT          The batch file that "starts" COGO
         2) COGO    .EXE          The preliminary .EXEcutable program
         3) COGO1   .EXE          The primary .EXEcutable program
         4) CONFIG  .EXE          Utility to configure default drives
         5) CONFIG  .DAT          Data file containing default program
                                  & data drive assignments (A and B)

                            COGO DOCUMENTATION DISK


         1) README  .BAT          The file that prints README.DOC
         2) README  .DOC          The preliminary print instructions
         3) TEST    .BAT          The file that prints TEST.DOC
         4) TEST    .DOC          The printer top-of-form/margin test
         5) PRINT   .BAT          The file that prints COGO.DOC
         6) COGO    .DOC          The primary DOCument/REFerence file
         7) CG234PRO.INP          A "PROper" sample BATCH file
         8) CG234COM.INP          A "COMmon" sample BATCH file


         Programs #2 through #5 of COGO PROGRAM DISK (the program
         disk)  M  U  S  T  be present so that the program functions
         properly.


         NOTE: For purposes of description, please consider your
               squeezed/combined disk (with the ARC.EXE program on it)
               to be the "DISTRIBUTION DISKETTE".

               The 2 diskettes that are produced from the DISTRIBUTION
               DISKETTE, containing the unsqueezed/separated COGO
               PROGRAM and DOCUMENTATION files will be called the
               "ORIGINAL" DISKETTES.

               As a point of clarification, the DISTRIBUTION diskette
               is simply a convenient medium with which we can get the
               package to you; the files on it are not intended to be
               run as COGO.  The two "original" diskettes that it
               'gives birth' to, however, are intended to be used as
               archive and working diskettes.






          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  13

                           BACKING UP YOUR DISKETTES

         The very first thing you must do is back-up your disks.
         Immediately place write-protect tabs on the "original" COGO
         disks; if you goof up, you will not have destroyed your (for
         now) only copies.  Have at least 6 blank diskettes ready and
         then perform the back-up as follows:

         1) FORMAT 2 BLANK SYSTEM DISKS:
            a) Place your DOS disk in drive A.
            b) Place a blank disk in drive B.
            c) Type FORMAT B:/S from the DOS ready prompt A>.
            d) Format one more disk this way, then answer "N"
               when you are asked to format a third disk.
         2) FORMAT 4 BLANK DATA DISKS:
            a) Place your DOS disk in drive A.
            b) Place a blank disk in drive B.
            c) Type FORMAT B: (not /S) from the DOS ready prompt A>.
            d) Format three (3) more disks this way, then answer "N"
               when you are asked to format a fifth data disk.
         3) CREATE 2 COPIES OF YOUR "ORIGINAL" COGO PROGRAM DISK:
            a) Place your "ORIGINAL" COGO PROGRAM DISK in drive A.
            b) Place one of your 2 formatted system disks in drive B.
            c) Type COPY *.* B:/V.  The "V" switch will verify copy.
            d) Remove disk from drive B and label "COGO BACKUP", put a
               write-protect tab on it, then squirrel it away to a
               safe place as your backup (never use it, just make more
               working copies with it).
            e) Make a second copy with the remaining blank system disk
               as per instructions 3a to 3c (above) but label this one
               "COGO WORKING COPY" and DO NOT USE A WRITE-PROTECT TAB.
            f) Remove "ORIGINAL COGO PROGRAM DISK" and put it away
               in a safe place as your "archive" copy (only to be used
               to make another COGO BACKUP disk if your backup copy
               becomes damaged).  You now have 2 program disk backups!
         4) CREATE 2 COPIES OF THE "ORIGINAL" COGO DOCUMENTATION DISK:
            a) Use 2 of the 4 data disks you formatted.
            b) Use instructions 3a to 3f (above) except label the
               copies COGO DOC BACKUP and COGO DOC WORKING COPY.
         5) Use the remaining 2 formatted non-system data disks to
            contain the COGO point files that you will create as you
            use COGO.  Label them "COGODATA #1" and "COGODATA #2".

         As a precaution, if any disks report "xxxx bad sectors" after
         formatting, get rid of them.  The cost of one floppy disk
         isn't worth the wear and tear on your nerves trying to figure
         out why the software isn't executing properly.

         ALWAYS KEEP SEVERAL BLANK FORMATTED "DATA" DISKS ON HAND! YOU
         NEVER WANT TO GET CAUGHT WITH A COMPUTER FULL OF COORDINATE
         VALUES AND NO DATA DISKS TO SAVE THEM TO, OR JUST AS BAD,
         DATA DISKS THAT DON'T QUITE HAVE ENOUGH ROOM.  ALSO, AS A
         PRECAUTION, ALWAYS MAKE BACKUPS OF YOUR IMPORTANT COORDINATE
         FILES TO A 2ND DATA DISK AND/OR TO A 2ND FILE NUMBER ON THE
         SAME DISK.  A LITTLE PRECAUTION CAN SAVE A LOT OF GRIEF.

         DO NOT WRITE-PROTECT YOUR WORKING COPY OF THE PROGRAM DISK!

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  14

                         CONFIGURING YOUR PROGRAM DISK


         Before running the COGO program, you should configure the
         disk drive assignments to your particular system.  As the
         disks are supplied, the program disk is defaulted to drive
         [A] and the data disk is defaulted to drive [B].

         To reconfigure:

         1) Place the COGO WORKING COPY program disk in drive [A].
         2) From the DOS ready prompt [A>], type: CONFIG
         3) Identify the disk drive which will contain your COGO
            program disk, then press the [RETURN] key.
         4) Identify the disk drive which will contain your coordinate
            data disks, then press the [RETURN] key.

         At the completion of this configuration routine, a file will
         be written to the COGO WORKING COPY program disk called
         CONFIG.DAT.  From this point on, every time you run the COGO
         program, file CONFIG.DAT will be searched and read.

         If you have a HARD DISK DRIVE, observe the above instructions
         exactly as stated (specifying drive "C" or "D" or... as the
         program drive and your choice of data drive "B" or "A" or...)
         then copy the contents of the entire program disk to your
         hard drive's subdirectory AFTER having first created that
         subdirectory and naming it COGO or whatever subdirectory name
         you choose.  For instructions on how to create a
         subdirectory, see the MKDIR command of your DOS manual.




























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  15

                               A HISTORY OF COGO


         Formally developed as a data input/output language for
         engineering/geometry/roadwork applications on computers,
         COordinate GeOmetry (COGO) was originally conceived by
         Professor Charles L. Miller of M.I.T. in 1959 on an I.B.M.
         705 mainframe computer, for use by the Puerto Rican Dept. of
         Public Works.  The first production version was implemented
         in 1960 for the IBM 1620 mainframe.  Dr. Miller's first COGO
         was a stunning achievement conceptually and practically,
         since it was made to work when the computers of the day were
         not generally capable of such applications.  The 1620 had a
         total memory of only 8K bytes, no disk or tape storage, could
         only add by looking up digits in an addition table, held 99
         points per job, occupied an entire room, and had less
         computing power than some of today's programmable hand
         calculators.

         The original COGO was revised and adapted by others; some of
         these versions being extremely popular improvements.  In
         1969, after five years of work, James R. Requa of Chas. H.
         Sells, Inc., Consulting Engineers & Surveyors, completed
         revisions on the original COGO source code.  Mr. Requa
         adapted the program to run on the newer I.B.M. model 1130
         mainframe and made many significant improvements and
         modifications to the source code.  These included adding
         about 50 commands, being able to hold 9,999 points per job,
         and the ability to output to a plotter.  Revisions and
         rewrites such as this helped to evolve today's COGO's into
         programs that are many times more powerful than the original.
         Of particular note, however, is the fact that the basic
         concepts, syntax, and vocabulary have remained essentially
         the same.  The modified program, SELLS COGO, was then
         formally placed into the "public domain" by Mr. Requa and
         Charles H. Sells, Inc.

         At that time, there was no requirement, need, or incentive to
         copyright software since the potential markets were almost
         non-existent - almost any organization with the capital to
         purchase a multi-million dollar computer could well afford
         programmers to design and write custom applications programs
         "in house", and usually did.  Most standard software was
         non-proprietary and usually "bundled" with the computer by
         the computer manufacturer, being particular to that unique
         computer system.  The purchase and/or use of "canned"
         software was the exception, since very little "plain vanilla"
         source code was written.  It was not considered that
         prepackaged software would be sold "off the shelf", and if
         you had mentioned to programmers of the day that software
         would be available on blister cards or shrink wrapped,
         hanging on wire-frame display racks, you would have been
         writing code in a padded room, since de-bundling was not even
         considered until the mid 1960's.  The albatross of copy
         protection did not then appear until the advent of the
         microcomputer and software mass marketing.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  16

                               A HISTORY OF COGO


         Mr. Requa's revised version of "SELLS COGO" for the I.B.M.
         1130 mainframe is the basis for GeoCalc's COGO, which is
         designed strictly for microcomputer operation and enhanced as
         described in this documentation.  GeoCalc's COGO was written
         in high and low level languages.

         It has been the experience of the authors of GeoCalc's COGO
         that most coordinate geometry programs are modeled after the
         original (in fact, many are almost exact replicas), but we
         have never seen the early pioneers who created the concept
         and methodology known as coordinate geometry properly
         credited, so we have taken this opportunity to do so.  Anyone
         who routinely crunches numbers on a grid, via computer, is
         indebted to all of those who took part in the creation of the
         first COGO's, particularly Dr. Miller and Mr. Requa.  The
         next time you leisurely and conveniently feed your known
         project data into the computer, press the [ENTER] key, then
         get 3 hours of calculations reduced to 30 seconds (and a
         printout to boot) using over 14 digits of numerical
         precision, tip one to the Miller development teams and a
         second to the Requa group.

         GeoCalc Software Systems Co., Inc.  would also like to thank
         Chas. H. Sells, Inc. and Mr. Ronald G. Leers (of Sells Inc.)
         for their aid and assistance; Dr. Charles L. Miller, who has
         continually improved and updated his COGO through his firm,
         CLM/Associates; and Mr. James Requa of TerraGraphics, who is
         likewise marketing a version of his original adaptation.  We
         especially thank all of these people for their time and
         assistance in providing us with the proper details and
         chronology of events from a developmental and historical
         perspective.























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  17

                      TERMINOLOGY, APPLICATION TECHNIQUES


         Since GeoCalc's COGO is an "Industry Specific" software
         package expressly for the needs of the surveying and
         engineering professions, no instruction or discussions of a
         tutorial nature on the theory or methodology of problem
         solutions is considered appropriate in this documentation.
         However, for any registered novices or registered
         institutions (such as colleges) with many novices or junior
         level technicians, GeoCalc Software Systems will be more than
         glad to provide telephone assistance and counseling on the
         techniques of using COGO in an efficient manner.

         Also, it will be assumed that generally accepted terminology
         or "buzzwords" need not be defined or explained; but, in the
         interests of standardization to avoid ambiguity, such
         "buzzwords" will be avoided where possible, and explained
         where necessary.

         Although many of the commands of COGO are quite powerful and
         complex, this documentation was designed to simply and
         clearly convey the exact function of those commands.  Because
         of the complex geometry intrinsic to many of the commands,
         sketches and drawings would most suitably supplement this
         documentation; in some cases, in fact, a sketch is almost
         vital.

         However, the logistics and physical nature of the
         distribution system which provided your GeoCalc COGO
         (Version 1.22) also prevents us from providing you with
         those necessary sketches.  By its very nature, this
         documentation file (COGO.DOC) is an ASCII file; it is
         designed simply and in a straightforward manner to output to
         most any printer on the market (and your monitor screen).  It
         is not as simple to make your printer mix text and graphics
         (required for sketches), if in fact your printer does have
         that capability.  Since we cannot provide sketches with
         version 1.22, they will be provided to registered users only,
         who will also receive the latest version's bound
         documentation.

         Educational institutions that register over 10 copies, in
         addition to receiving discounted registration fees, will
         also receive a COGO course outline for purposes of installing
         a 12 week COordinate GeOmetry/CADD course in their
         curriculum.  This will also be accompanied by an expanded
         BATCH disk which will demonstrate in greater detail the
         commands of COGO (a "show N' tell").  Also, COGO->CADD
         demonstrations will be included.








          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  18

                           BOOTING THE COGO PROGRAM


         If the instructions for making backups of your original
         distribution disk have been followed, you now have four
         working diskettes (plus your DOS disk) on hand:

                        1) The COGO WORKING COPY
                        2) The COGO DOC WORKING COPY
                        3) 2 blank formatted data disks.
                                      plus
                              Your system (DOS) disk

         1) OUTPUT THE DOCUMENTATION TO YOUR PRINTER.

            a) Place your DOS disk in drive A.
            b) Turn the computer on and answer the DOS prompts.
            c) Place the COGO DOC WORKING COPY in drive A.
            d) Type README, then press the [RETURN] key.
            e) Follow the instructions.  Remove DOC disk when done.

         2) "BOOT-UP" THE COGO PROGRAM.

         The COGO PROGRAM disk should contain file AUTOEXEC.BAT.  This
         automatically gets COGO running if the COGO WORKING COPY
         program disk is in the default drive when the computer is
         powered up.  It contains the command: COGO.

         To run COGO from a cold start (the computer is off):

            a) Place your COGO WORKING COPY  disk in drive A.
            d) Place a blank, formatted data disk in drive B.
            b) Turn the computer on.  Execution is automatic.

         In the event the AUTOEXEC.BAT file is missing, create it
         yourself (consult your DOS manual), or, do the following:

            a) Place your COGO WORKING COPY program disk in drive A.
            d) Place a blank, formatted data disk in drive B.
            b) Turn the computer on and answer the DOS prompts.
            f) At the DOS A> prompt, type COGO, then [RETURN].

         NOTE: For multi or hard disk systems, the program will save
               cogo files and data to the DEFAULT DATA DRIVE specified
               during the configuration process.  This drive may (or
               may not) be the hard drive.

         The COGO program will load into the computer, an introductory
         screen will display briefly, then you will find the cursor
         flashing next to the COGO prompt (>>).  At this point you may
         start a COGO job (S O J ###), or, press the ALT+Z key
         combination to find out what commands are available.

                   *****************************************
                   * DO NOT WRITE-PROTECT THE PROGRAM DISK *
                   *****************************************


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  19

                                   PLOTTING

         All versions of COGO sent to registered users will be
         supplied with a stand-alone CADD (Computer Aided Design &
         Drafting) program which will accept the coordinate files
         created by GeoCalc's COGO.  It will also allow you to draw
         and/or plot the COGO figures on your plotter or dot matrix
         printer, including layering of up to 256 levels of figures
         and/or structures in layers, creation/design/placement of
         text, zooming, rotation, etc.

                              FLIP-UP CALCULATOR

         Registered users of COGO will also receive a "flip-up",
         RAM-resident HP-11C RPN programmable calculator emulator
         which places a complete, functional HP-11C clone on the
         screen.  It has 20 data memories (which can be screen
         listed), 4 stack registers (which can be screen listed), and
         a 500 step program memory (which can be listed to screen or
         printer and/or saved/loaded to diskette).

                             NOTEPAD TEXT EDITOR

         All registered versions of COGO will be sent with the "NOTEPAD"
         RAM-resident word processor.  This will allow immediate
         creation of batch files while WITHIN the COGO program without
         having to exit to separate editors or word processors.

                                 DOS FUNCTIONS

         Registered user's versions will also allow you to address the
         DOS functions such as COPY, DIR, RENAME, ERASE, FORMAT, etc.
         without leaving COGO.  You can format a fresh disk, for
         example, while still in COGO, then save coordinates to it.

                              SHAREWARE EXCLUSION

         Because of proprietary considerations, both the CADD system
         and HP-11C Calculator emulator are NOT included with this
         version 1.22 of COGO through public domain distribution
         channels, but registered users may receive both the CADD
         system and the Calculator with the latest version of COGO.

                              BOUND DOCUMENTATION

         Registered users will also receive a bound, annotated/revised
         copy of this documentation with the latest version of COGO,
         containing sketches and drawings depicting the geometry of
         worked examples.

                                 LATER CHANGES

         GeoCalc Software Systems Company, Inc. reserves the right to
         alter or amend its products or offerings.  However, this will
         not be done without re-releasing version 1.22 through the
         "Public Domain" software distribution network to "announce"
         significant changes, if so warranted.

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  20

                            GENERAL FILE STRUCTURE

         All coordinates that are created by COGO may be saved to the
         data disk in the default drive (which we will assume will be
         drive B from now on) under an identifying filename.  This
         filename takes the form of a 3-digit FILE NUMBER that
         uniquely identifies your coordinate file as it resides on the
         data disk.  The FILE NUMBER consists of any three-digit
         number in the range 1 to 999.  When the file is first created
         on the data disk, COGO will prefix the letters "CG" to your
         file number automatically, in the form CGxxx.  A typical disk
         directory's COGO data files may look like this:

                      ...................................
                      ...................................
                      ...................................
                      CG135     1024   11-27-86    12:02p
                      CG557     3273    1-17-87     2:42p
                      CG004    32051   10-23-86    10:15a
                      CG669      256    1-20-87     1:05p
                      CG085      512    1-20-87    11:42a
                      ...................................
                      ...................................

         GeoCalc's COGO files are structured so as to contain all
         relevant information internally in a single file, each of
         which has three distinct elements:

                         1) The header/label section.
                         2) The coordinate section.
                         3) The figure section.

         Some COGO's use 2 or 3 separate disk files to contain the
         header, figure, and coordinate information (as opposed to 1
         single file).  The benefits of using a single file to contain
         this information was given much consideration and adopted for
         use in GeoCalc's COGO on the basis that:

                    1) Your disks are much less cluttered
                       (and much more organized/readable)
                    2) Your disks can hold more files
                       (physically and logically)
                    3) Your disks can hold more coordinates

         Items 2 and 3 may seem redundant at first, but it must be
         considered that using DOS 2.0+ without the use of
         sub-directories, only 128 files total can be saved to any one
         disk.  The file names are stored in what is known as the
         disk's [F]ile [A]llocation [T]able which can only hold 128
         entries per directory.  Thus, if 3 or more files are created
         for each COGO job, then the maximum number of COGO jobs that
         can be saved to disk is 128/3 = 40+ jobs, if you consider
         only the available space in the FAT.





          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  21

                            GENERAL FILE STRUCTURE

         Although it is of little concern to most of us, there are 2
         different ways to fill up a disk; by filling up the FAT with
         up to 128 filenames, or, filling up the disk with over 362Kb
         of data.  You will in fact run out of disk space if you have
         128 COGO files of 50 bytes each (a total of only 6,400 bytes
         on the disk), or, if you have only 1 file that exceeds
         362,000 bytes.

         Other COGO's often require you to pre-define the size of your
         data files, establishing a maximum size, before you run the
         job.  This partitions the disk by setting aside the space for
         that amount of coordinates before they are created.  However,
         if you estimate too high, you have wasted data space; if you
         estimate too low, you must re-define the space allocation.

         GeoCalc's COGO has a "dynamic" file allocation structure; it
         assigns disk space to data as it is created, not before.  The
         user therefore need not be concerned with fixing or
         estimating the size of the file before it is created.  In
         this way, all file functions are "invisible" to the user who
         may run his jobs and conduct his business without having to
         be bothered with messy maintenance tasks.  The trade-off is
         that file access is relatively slower for large files;
         however, since the slowdown is not appreciable and large
         files are the exception rather than the rule, we considered
         this a minor factor (although a speedup is being worked on).

                         SPECIFYING AND USING FIGURES

         During the course of a COGO job, all coordinates that define
         points are created and assigned to point numbers.  At the
         completion of the job, all these point numbers and
         coordinates are saved to disk when you invoke the END OF JOB
         or END OF RUN commands.  Occasionally, however, you may find
         it necessary to use those commands that treat entire figures
         as a single entity.  In most cases, you can describe the
         figure (which may only be a small part of the entire
         coordinate file) as a string of point numbers.  For example,
         the AREA command is invoked thusly:

                      AREA (34 15 23 45 78 901 17 23 34)

         From this command, the area of the figure defined by points
         34, 15, 23, 45, 78, 901, 17, 23, and back to 34 again is
         computed.  For small figures, this is a convenient and
         efficient data entry format.  However, what if the figure
         were large; defined by 50 or 100 points instead of only 7 ?
         Having to enter 50 or 100 numbers each time you invoked a
         command would be a severe inconvenience.  Fortunately, a
         method exists so that one or more individual figures can be
         defined WITHIN a coordinate file.

         ************************************************************
         *   KEEP YOUR FIGURE NUMBERS NUMERICALLY LOW (FOR SPEED)   *
         ************************************************************

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  22

                         SPECIFYING AND USING FIGURES

         By using the command STORE FIGURE, you can specify any group
         of points (up to 999, which may repeat - for a total of 9999)
         as a figure.  In fact, you can specify more than 1 figure (up
         to 99) in any coordinate file.  These figures could be
         thought of as pseudo-files, in the sense that they are unique
         definitions of geometric figures; they are not, however,
         coordinate files in themselves.  A figure, as it resides
         within the coordinate file on disk, simply contains the point
         numbers (but not coordinate values) of the points defining
         the angles of your figure arranged in the order which you
         have specified.  As an example, suppose you have created a
         subdivision containing 12 individual parcels.  All angle
         points of all parcels, including street centerline
         intersections, have been defined and assigned point numbers
         from 1 to 87.  The coordinates of 4-sided parcel #1 are
         numbered 5, 64, 4, and 17; the coordinates of 7 sided parcel
         #7 are 6, 9, 27, 3, 82, 11, and 14.  Each of these parcels
         may be individually specified as a figure.  They can be
         retrieved at a later time whenever the same FILE NUMBER is
         accessed.  The command STORE FIGURE 1 (5 64 4 17 5) would
         create figure #1.  STORE FIGURE 7 (6 9 27 3 82 11 14 6) would
         likewise create figure #7.  Figure #'s are then used instead,
         i.e. AREA BEARINGS 7 or TRAVERSE ANGLES 1.

                       CURVE DEFINITIONS WITHIN FIGURES

         Also, curves may be defined within the structure of the
         figure definition.  For example, traversing along a tangent
         from point #6 to point #9, extending along a back tangent to
         "Point of Curvature" #27, extending at a right angle (to the
         left) to the Vertex of a vertex point #3, extending at a
         right angle (to the right) to "Point of Tangency" point #82,
         extending along the foreward tangent to a point on foreward
         tangent #11, then back to point #6 describes a curve:

         9 --------- 27(PC)                 By using the following
         |           |                      format, this curve can
         |           | -Radii               be defined within the
         |           |   |                  figure:
         |        (V)3 ---- 82(PT)
         |                  |                          PC  V  PC
         |                  |           STO FIG 1 (6 9 27 C3L 82 11 6)
         |                  |                             ^ ^
         | POB              |
         6 ---------------- 11

         Note that the PC is followed by the letter C (Center of
         Curve) immediately followed by the point number of the Vertex
         (3) immediately followed by the direction of the arc (to the
         right - R).  When this format is used to define a curve
         within a figure, it is treated as a curve in all applicable
         calculations.  In this particular example, the AREA command
         AREA 1 would give the area of the above specified figure
         including or excluding the segment of the arc.  See the
         instructions for the command STORE FIGURE and page 31.

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  23

                                 COMMAND LIST

       No.  COMMAND                     No.  COMMAND
       ~~~  ~~~~~~~~~~~~~~~~~~~~~~~~~~  ~~~  ~~~~~~~~~~~~~~~~~~~~~~~~~

         1  Adjust Area                  51  Locate Angle
         2  Alignment                    52  Locate Azimuth
         3  Alignment Offset             53  Locate Bearing
         4  Angles                       54  Locate Deflection
         5  Arc Arc Intersect            55  Locate From Alignment
         6  Arc Line Azimuth             56  Locate Line
         7  Arc Line Bearing             57  Offset Alignment
         8  Arc Line Points              58
         9  Area                         59  Parallel Figure
        10  Area Azimuth                 60  Parallel Line
        11  Area Bearing                 61  Points Azimuth Intersect
        12  Azimuth Intersect            62  Points Bearing Intersect
        13                               63  Points Intersect
        14                               64  Points On Alignment
        15                               65  Redefine
        16  Batch Print                  66  Segment
        17  Batch Screen                 67  Segment Plus
        18  Bearing Intersect            68  Segment Minus
        19  Compound Spiral              69  Simple Curve
        20  Convert Meridian             70  Simple Spiral
        21  Coordinate Offset            71  Spiral Length
        22  Coordinate Point on Arc      72  Spiral Offset
        23  Coordinate Point on Spiral   73  Spiral Spiral
        24  Copy File                    74  Start Of Job
        25  Curve Spiral                 75  Station And Offset
        26  Define Curve                 76  Station From Coordinates
        27  Delete Coordinates           77  Store
        28  Delete Figure                78  Store Figure
        29  Describe Alignment Azimuth   79  Store Job
        30  Describe Alignment Bearing   80  Streets Intersect
        31  Distance                     81
        32  Divide Arc                   82  Tangent
        33  Divide Figure                83  Tangent Offset
        34  Divide Line                  84  Traverse Angles
        35  End Of Job                   85  Traverse Azimuths
        36  End Of Run                   86  Traverse Bearings
        37  Extend Arc                   87  Traverse Deflections
        38  Figure Arc Intersect         88  Type Print
        39  Figure Figure Intersect      89  Type Screen
        40  Figure Line Intersect
        41  Fit Alignment
        42  Fit Curve                    ALT Z - Main Menu
        43  Get Coordinates              ALT F - In/Ft Table
        44  Get Figures
        45  Inverse Azimuth        ----------------------------------
        46  Inverse Bearing       |  NOTE:  The menu, as it appears  |
        47  Line Spiral           |           on the screen when     |
        48  List Coordinates      |            invoked by ALT+Z,     |
        49  List Figures          |          is listed on page 32.   |
        50  List Files             ----------------------------------



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  24

                         GEOCALC'S COGO - AN OVERVIEW


         COGO, or COordinate GeOmetry, is a formal, defined system of
         data entry which accepts input variables and then outputs
         calculated resultants; all computations, input, and output
         are relative to a coordinate grid assumed by the operator.

         For those who have not yet been exposed to COGO, it can be
         thought of as a programming language in much the same sense
         that you "program" your hand calculator to resolve problems.
         Generally, most COGO applications programs fall into two
         standard categories: COMMAND GENERATED and MENU GENERATED.

         COMMAND GENERATED COGO's are intrinsically efficient after
         the "language" of the data input/output is learned, since a
         1-line command will accomplish the function.  For example, to
         assign a coordinate value from point #1 to point #2, with a
         bearing of N 24 13 17.25 W and a course distance of 1245.678,
         you typically will type the following (on 1 line):

                  LOCATE BEARING 1 2 N 24 13 17.25 W 1245.678
                                [Press RETURN]

         If the known coordinates of point #1 were N 1000.0000 and
         E1000.0000, the coordinates N 2136.0166 & E 488.9424
         would then appear on the screen.  There are no menus to
         select and all functions are immediately available.  However,
         expertise in using the program must be attained and
         maintained.  Also, few command oriented COGO's allow data
         input strictly from the numeric keypad.  For the non-typist
         (or even a true peck artist) this slows down the rate of data
         entry by making you alternately jump between the QWERTY
         (alphabetic) and numeric keypads when you really should be
         concentrating on your project geometry and data input/output,
         using the numeric keypad wherever and whenever possible.

         MENU GENERATED COGO's are ordinarily considered superior for
         the occasional user or beginner, since all functions are
         "prompted" on the screen, usually by selecting menu numbers.
         The user is then led step-by-step through the data entry
         process, entering input data exclusively through the numeric
         keypad and menu choices mostly via the numeric keypad.

         GeoCalc's COGO represents many hours of design and coding
         with the goal of producing a convenient yet efficient method
         of data entry and resultant display.  It is a standard
         COMMAND GENERATED COGO with the advantages inherent to that
         type, while also being a MENU GENERATED COGO for those
         unwilling to commit the commands to memory.  In fact, as
         later described, the commands can be accomplished by either
         typing them (or their abbreviations) or by using a
         menu-selected numerical code.  In this manner, we have hoped
         to present as versatile and convenient a package as possible
         so that everyone would find the program as easy-to-learn AND
         efficient as it could possibly be.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  25

                         GEOCALC'S COGO - AN OVERVIEW


         There are several restrictions to version 1.22 that should be
         recognized:

            1) There is a limit of 999 points & 99 figures per file.
            2) No balancing or error distribution is supported.
            3) No screen, printer, or plotter drawing is supported.
            4) No sketches or worked examples are illustrated.

         All of these limits and restrictions are removed in versions
         sent to registered users.

         During the design and coding of GeoCalc's COGO, special
         efforts were made to make the overall program less cryptic
         and intimidating than some COGO's we have seen (and fondly
         used).  This was accomplished by use of the Main Menu, which
         is otherwise known as a "flip-up".  By simply pressing the
         ALT and Z keys, a full menu of all command choices will
         flip-up; pressing the ALT+Z combination again will then make
         it flip-down.  The on-screen menu is thus available at all
         times for those who are not sure of their commands.

                                 ON-LINE HELP
                            (Registered Users Only)

         At any time (except during data input), you may access
         on-line help by typing a question mark, followed by the menu
         number of the command you need help with.  For example,
         suppose you forget the input format for the command ARC LINE
         AZIMUTH.  First, make sure the menu number is correct by
         calling the menu (ALT+Z).  The menu number is 6.  Now, just
         type  ?6  and press [RETURN].  The help file will display:

         -----------------------------------------------------------
        |                      ARC LINE AZIMUTH                     |
        |                                                           |
        |  No  Command   Description                                |
        |  ~~  ~~~~~~~~~ ~~~~~~~~~~~                                |
        |   6  A L A     I  V R  P  A  M  /  OFF                    |
        |                                                           |
        |  Locate point I by intersecting a circle whose vertex is  |
        |  at V and whose radius is R, with the line through point  |
        |  P on an azimuth (or optionally, a bearing) of A. OFF is  |
        |  an optional offset distance of the azimuth line.  +M is  |
        |  a specified  point # closest to the intended intersect,  |
        |  & -M is a specified point  # farthest from the intended  |
        |  intersect.                                               |
        |                                                           |
        |  >>_                                                      |
         -----------------------------------------------------------

         The help file will remain on the screen until it scrolls off
         naturally.



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  26

                         GEOCALC'S COGO - AN OVERVIEW


         Although no file storage (except CONFIG.DAT) should occur on
         the COGO WORKING COPY program disk, don't put a write-protect
         tab on this disk.  Certain initialization procedures during
         COGO startup require the ability to write to the program disk
         for internal/system purposes.


                        *******************************
                        *                             *
                        *     DON'T WRITE-PROTECT     *
                        *      THE PROGRAM DISK!      *
                        *                             *
                        *******************************


         Although mentioned at other points throughout this
         documentation, you are again cautioned that the ONLY way to
         end the COGO program is by calling the END OF RUN command.
         If you exit by any other means, you will almost certainly
         lose any coordinates you may have created.


              **************************************************
              *  EXIT COGO VIA THE "END OF RUN" COMMAND ONLY!  *
              **************************************************


                            RAM-RESIDENT UTILITIES

         An additional caveat concerns "RAM resident" utilities: be
         extremely careful which ones you use, the order in which they
         are "loaded", and their effect on and compatability with
         COGO.  The HP-11C emulator works fine with COGO, and so does
         Borland's Sidekick (load the HP-11C emulator first, Sidekick
         second); but change the HP-11C emulator "hot keys" to
         [ALT]+[X].  We have found that other "RAM resident" utilities
         can produce some extremely erratic activity with COGO.
         Before you use any utility other than (or with) Sidekick &/or
         the calculator emulator, try it out under all possible
         conditions.  To go a step further, we don't recommend any
         utilities (including such seemingly innocent and innocuous
         creatures as print spoolers) other than the HP-11C emulator.













          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  27

                             OPERATING CONVENTIONS

         INPUT
         -----
         Input consists of a COMMAND in the "language" of COGO,
         followed by the specified input data particular to that
         command, as described in the command descriptions.  Input is
         normally interactive through the keyboard, or may be
         "batched" via ASCII (.INP) files on the data diskette.

         MISSING DATA
         ------------
         If a command is entered without variables or data, then
         processing will not occur and 2 BEEPs will sound; you must
         now LEAVE COLUMN #1 OF THE NEXT LINE BLANK in order for COGO
         to accept the input data.  Likewise for multi-line input.
         However, if you mistakenly enter a data value (from 1 to 99)
         in that 1st column, COGO will assume a new command, which
         could cause an unintended blunder of major proportions.

         COMMENTS
         --------
         If there is an asterisk (*) anywhere on the input line,
         anything typed after the asterisk will be reproduced as
         comments in the output.  If there are two asterisks (**) in
         the 1st and 2nd columns, anything typed after the asterisks
         will be reproduced as comments on the top of the next output
         page.  A comment may occupy an entire line by itself, or may
         follow the last data item on a line (similar to the REMark
         function of the BASIC programming language).

         ABBREVIATIONS
         -------------
         All commands can be entered by using abbreviations of those
         commands.  At least the 1st letter of each command word must
         be entered plus enough additional letters to uniquely
         identify that command.  The command words (or abbreviated
         words) must be separated by spaces.  For example to LOCATE
         BEARING, you may use LOC BEAR, LC BE, L BRG, L BG, etc. If
         the abbreviation is ambiguous, it will not be accepted.

         COMMAND CODES
         -------------
         To make life a little more exciting for those who crave coded
         commands, all of the commands have numeric equivalents.  All
         commands can thus be entered using their code numbers, in
         conjunction with the flip-up menu.  For example, to perform
         ARC LINE BEARING just type a 7, then the input variables.

         PRECISION
         ---------
         Although the original 1160 COGO was limited to a precision of
         9 significant digits (which was somewhat improved by origin
         reduction techniques to 12 digits), all calculations in
         GeoCalc's COGO are performed to 14 significant digits of
         precision.  Output displays may be rounded (distances,
         coordinates, & stationing to 4 places, angles to 3 places,
         etc.) but they are still computed to full 14 digit precision.

          GeoCalc COGO - Surveying/Engineering Applications Software




                                                              Page  28

                             OPERATING CONVENTIONS


         STATIONING
         ----------
         Stationing is entered, where applicable, as decimal feet.
         For example, STAtion 12+34.567 is entered as 1234.567 feet.

         OUTPUT
         ------
         Output is to the screen, printer, or disk.

         ANGULAR (DMS FORMAT)
         --------------------
         Angles or directions must be entered in degrees, minutes, and
         seconds format with spaces between them.  For example, 45 25
         23.23 would be valid.  If you wish to omit seconds, simply
         terminate the minutes with a decimal point; such as 45 25.
         If you wish to omit minutes and seconds, simply terminate the
         degrees with a decimal point, such as 45. or 7.

         BEARINGS
         --------
         Bearings may be entered by prefixing and suffixing them with
         their cardinal directions: N E S W.  For example N 45 25. W,
         or S23 23 45.23E.

         QUADRANT CODES
         --------------
         So that an entire job can almost be run from the numeric
         keypad only, COGO will allow input bearings to be identified
         by their quadrant numbers: 1=Northeast, 2=Southeast,
         3=Southwest, 4=Northwest.  If quadrant numbers are
         chosen, you will be able to enter the line directions from
         the numeric keypad instead of having to enter the cardinal
         directions from the QWERTY keypad.

         AZIMUTHS
         --------
         Azimuths are measured clockwise from north and are entered
         according to the rules for angular input as described above.

         DIRECTION SIGN
         --------------
         Angles/azimuths right/clockwise are entered as positive
         values; angles/azimuths left/counterclockwise are entered by
         preceding the degrees (only) with a minus sign.

         ANGULAR EXPRESSIONS
         -------------------
         You may input angles/directions by specifying them as
         expressions within parentheses.  The expression may include
         addition and/or subtraction of angles/directions.  Bearings,
         however, must be specified by their cardinal directions of
         N S E W (not quadrant numbers).



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  29

                             OPERATING CONVENTIONS


         ANGULAR DELIMITERS
         ------------------
         You may enter angles/directions indirectly by use of the
         delimiters "A" for azimuths or bearings, and "G" for angles.
         The input format for azimuths or bearings is A BP# FP#, where
         A is the azimuth or bearing delimiter, BP# is the back point
         number of the direction, and FP# is the foreward point number
         of the direction.  To input angles, use format G BP# AP# FP#,
         where G is the angle delimiter, BP# is the backsight point
         number, AP# is the angle point number, and FP# is the
         foresight point number.

         DISTANCE
         --------
         Distances may be entered as is, or as with angles/directions,
         as an expression in parentheses.  The input distances may be
         summed as: (300+200-137.254).  A negative distance will also
         create a back extension of a line.

         DISTANCE DELIMITER
         -----------------
         The use of the "D" distance delimiter allows a distance
         between two points to be entered even if the actual distance
         is not known.  For example: D 23 24 will input the distance,
         indirectly, from point #23 to point #24.

         REPEATABILITY
         -------------
         All commands (except control commands) may be repeated
         without having to reenter the command (or its code #).  When
         a command is entered in the normal manner and is executed, a
         repetition of that command using different variables is
         possible without having to re-type the command.  After the
         command is executed the 1st time, simply type a space in
         place of the command (press the [SPACE BAR] one time) then
         enter the new variables.  When COGO sees this single space,
         the prior command will always be executed for as many times
         as the blank space occupies the 1st column of succeeding
         input strings (applies to .INP files for batching, too).

         As previously stated, the directions and distances may be
         indirectly input, as follows:

         DELIMITER  EXAMPLES  DESCRIPTION
         ~~~~~~~~~ ~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
             D        D 1 7   Denotes a straight line distance from
                              point 1 to point 7.

             A        A 3 6   Denotes the azimuth or bearing from
                              point 3 to point 6.

             G      G 1 4 9   Denotes the angle at point 4, clockwise
                              from 1 to 9.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  30

                             OPERATING CONVENTIONS


         EXAMPLES OF ANGULAR/DISTANCE INPUT
         ----------------------------------

         227                      Distance of 227 feet
         227.23458431             Distance of 227.23458431 feet
         (227.234584)             Distance of 227.234584 feet
         D 23 85                  Distance between points #23 and #85
         (227 + 50.23)            Distance sum of 227 and 50.23 feet
         (50 - 20 + 10)           Distance of 40 feet
         (D 25 30 + 227)          Distance between points #25 and #30
                                           summed to 227 feet
         -43.                     43 deg
         43 03.                   43 deg, 3 min
         43 23 05.7               43 deg, 23 min, 5.7 sec
         -55 23.                  55 deg, 23 min angle (CCW) left
         90 00 00.00              90 deg angle (CW) right
         90 0 0                   90 deg angle (CW) right
         +90 0 0                  90 deg angle (CW) right
         G 234 235 236            Angle right (CW) at point 235, from
                                           point 234 to point 236
         (A 235 235 - 230.)       Angle between azimuth from points
                                           235 to 236, and azimuth of
                                           230 degrees
         S 23 23 23 W             BRG S 23 deg 23 min 23 sec W
         S23 23 23W               BRG S 23 deg 23 min 23 sec W
         S23 23 23.4E             BRG S 23 deg 23 min 23.4 sec E
         N 0. E                   DUE NORTH
         N 0. W                   DUE NORTH
         1 0.                     DUE NORTH (Quad #)
         N 90. E                  DUE EAST
         S 90. E                  DUE EAST
         1 90.                    DUE EAST (Quad #)
         S 0. E                   DUE SOUTH
         S 0. W                   DUE SOUTH
         2 0.                     DUE SOUTH (Quad #)
         S 90. W                  DUE WEST
         N 90. W                  DUE WEST
         3 90.                    DUE WEST (Quad #)
         3 23 23 23.5             BRG S 23 deg 23 min 23.5 sec W
         A 235 678                BRG from point 235 to point 678
         (S45.W + A 5 8 - A 3 4)  BRG S 45 deg W plus the angle
                                           between courses 5 to 8 and
                                           3 to 4






                    NOTE: At any point in the instructions,
                            CCW = Counterclockwise
                             CW = Clockwise



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  31

                             OPERATING CONVENTIONS


         FIGURES
         -------
         Figures are explained in great detail on page 22.  However,
         is should be noted that whenever possible, you should specify
         all or part of your coordinate files as figures.  Using
         figures in COGO commands, as opposed to point numbers, is the
         most efficient way to manipulate the coordinates.  Note the
         number of COGO commands that require a coordinate "DESC" as
         input.  In all cases, "DESC" may be a string of point numbers
         OR it can be a single figure number.  Obviously, using figure
         numbers is much preferable to dealing with whole strings of
         point numbers.

         FIGURE TRANSPOSITIONS
         ---------------------
         For all commands that use figures as input data, you may
         reverse, or transpose the point numbers by following the
         figure number or description with the letter (T).  This
         produces the effect of having entered the points in reversed
         order (although it does not permanently alter their order).
         For example, using the figure #1 (of above), the command
         INVERSE BEARING 1 T would output the bearings/distances in
         the order 1 5 4 3 2 1.

         UPPER CASE LOCK
         ---------------

         COGO recognizes only upper case input for all commands and
         data.  So that this requirement poses no inconvenience, the
         program will automatically shift the [CapsLock] to upper
         case.  The [NumLock] toggle, however, will not be altered; it
         will remain in cursor control mode as the default.  Of course
         you can choose between number mode (for quick COGO input) or
         cursor mode (for use in memory-resident utilities such as
         SIDEKICK).  Please note that your [CapsLock] key's LED will
         not reflect the CAPS ON status (if your keyboard is so
         equipped).  When COGO is exited in the normal manner via END
         OF RUN, the [CapsLock] will be revoked to its default state
         of [CapsLock] off.  We realize that this little ammenity is
         not a particularly earthshaking feature, but it will help to
         prevent mental disintegration brought on by continually
         forgetting to manually toggle [CapsLock] when you first power
         up (such as the authors experienced with other COGO's).

         COORDINATE AREA / FIGURE AREA
         ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         If, during the S O J, you find that your figure area is equal
         to or greater than the coordinate area, store a dummy value
         in a point number 50 or 100 points higher than your highest
         point number.  Better yet, create all of your coordinate
         points, if not the majority, before you create figures.  We
         make these recommendations so that your file access will be
         efficient and free of errors.  DON'T LET THE COORDINATE AREA
         GET EQUAL TO OR GREATER THAN THE FIGURE AREA!

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  32

                              THE "FLIP UP" MENU

                                  [ALT] + [Z]



                           GeoCalc's COGO - Main Menu

       1 Adj Area  21 Cord Off  41 Fit Align 61 PtsAzInt  81
       2 Alignment 22 Cord POA  42 Fit Curve 62 PtsBrgInt 82 Tangent
       3 Ali Off   23 Cord POSP 43 Get Cords 63 Pts Int   83 Tan Off
       4 Angles    24 Copy File 44 Get Fig   64 PtsOnAli  84 Trav Ang
       5 ArcArcInt 25 Crv Sprl  45 Inv Az    65 Redefine  85 Trav Az
       6 ArcLinAz  26 Def Curve 46 Inv Brgs  66 Segment   86 Trav Brg
       7 ArcLinBrg 27 Del Cords 47 Line Sprl 67 SgmtPlus  87 Trav Dfl
       8 ArcLinPts 28 Del Fig   48 List Cord 68 SgmtMinus 88 Type Prt
       9 Area      29 DesAliAz  49 List Fig  69 Smpl Curv 89 Type Scrn
      10 Area Az   30 DesAliBrg 50 List File 70 Smpl Sprl
      11 Area Brg  31 Distance  51 Loc Angle 71 Sprl Lgth
      12 Az Int    32 Div Arc   52 Loc Az    72 Sprl Off
      13           33 Div Fig   53 Loc Brg   73 Sprl Sprl
      14           34 Div Line  54 Loc Defl  74 StrtOfJob
      15           35 EndOfJob  55 LocFrmAli 75 StaAndOff
      16 Batch Prt 36 EndOfRun  56 Loc Line  76 StaFrmCrd
      17 Batch Scr 37 Extnd Arc 57 Off Align 77 Store
      18 Brg Int   38 FigArcInt 58           78 Sto Fig
      19 Cmpd Sprl 39 FigFigInt 59 Par Fig   79 Sto Job    ALT+Z Menu
      20 Conv Merd 40 FigLinInt 60 Par Line  80 Sts Int    ALT+F In/Ft




                   THE "FLIP UP" INCH/FOOT CONVERSION TABLE

         For those who haven't yet mastered the mental gymnastics of
         converting inches to and from decimal feet, a simple
         "flip-up" conversion table is available by pressing the [ALT]
         and [F] keys simultaneously.  This table displays whole and
         fractional inches to sixteenths of an inch and their decimal
         equivalents to 3 decimal places of a foot.  To "flip-down"
         the table and return to the unaltered COGO screen, press
         [ALT]+[F] again.  Alternately, registered user's versions
         include a program that can be called interactively from
         within COGO to make the conversions via the on-screen
         "HP-11C" calculator emulator and "export" the converted
         numbers to the last position of the COGO cursor.  Although
         its not as sexy, we like the flip-up better.











          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  33

                               CONTROL COMMANDS
                               ~~~~~~~~~~~~~~~~

         Control commands are used to control COGO's jobs and files
         (and the flow of those files) by specifying the input/output
         devices.  Control commands have two unique characteristics:

         a) The command is processed between or during a job; other
            commands are processed only during a job.
         b) Control commands have no repeatability; if a blank command
            follows a control command, it will not be interpreted as
            being the same command.

         The control commands are:

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~    ~~  ~~~~~~~~~~~~~~~~~~~~~~~~~
         74  Start Of Job              17  Batch Screen
         35  End Of Job                16  Batch Print
         36  End Of Run                88  Type Print
                                       89  Type Screen



                           FILE MAINTENANCE COMMANDS
                           ~~~~~~~~~~~~~~~~~~~~~~~~~

         COGO allows both temporary and permanent storage of data
         files whose contents may be listed or copied.

         The file maintenance commands are:

                           #  NAME
                          ~~  ~~~~~~~~~~~~~~~~~~~~~~
                          50  List File
                          24  Copy File
                          79  Store Job


                          POINTS MANTENANCE COMMANDS
                          ~~~~~~~~~~~~~~~~~~~~~~~~~~

         These provide the ability to transfer coordinate values of
         points from one media to another.  They do not provide
         geometric functions.

         The points maintenance commands are:

                           #  NAME
                          ~~  ~~~~~~~~~~~~~~~~~~~~~~~
                          77  Store
                          65  Redefine
                          43  Get Coordinates
                          27  Delete Coordinates




          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  34

                          FIGURE MAINTENANCE COMMANDS
                          ~~~~~~~~~~~~~~~~~~~~~~~~~~~

         These provide the ability to transfer figures from one media
         to another.  They do not provide geometric functions.  Note
         that a figure is composed only of a "string" of point numbers
         and not the actual coordinate values of those points, and is
         no more than a list of integers and delimiters.  This
         "string" can describe not only a figure, such as a closed
         traverse, but also a group of figures.

         The figure maintenance commands are:

                           #  NAME
                          ~~  ~~~~~~~~~~~~~~~~~~~~~~~
                          78  Store Figure
                          44  Get Figures
                          28  Delete Figures



                        LINE & CURVE EXTENSION COMMANDS
                        ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

         These commands generally provide the assignment of coordinate
         values to user-specified points based on given directions and
         distances from known points.  Together with the intersection
         type commands, they comprise the bulk of COGO's geometric
         power and utility.  Their use is enhanced by angular and
         distance delimiters and expressions.

         The line and curve extension commands are:

                           #  NAME
                          ~~  ~~~~~~~~~~~~~~~~~~~~~~~
                          37  Extend Arc
                          51  Locate Angle
                          52  Locate Azimuth
                          53  Locate Bearing
                          54  Locate Deflection
                          56  Locate Line



                             POINTS MOVE COMMANDS
                             ~~~~~~~~~~~~~~~~~~~~

         These commands replace original coordinate values of points
         with new values.  CAUTION and CARE is urged since they
         permanently alter coordinate values.

         The points move commands are:

                           #  NAME
                          ~~  ~~~~~~~~~~~~~~~~~~~~~~
                          20  Convert Meridian
                           1  Adjust Area

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  35

                          POINTS DEFINITION COMMANDS
                          ~~~~~~~~~~~~~~~~~~~~~~~~~~

         These are the "redundant" commands, which will generally
         allow a more convenient and efficient geometric solution to a
         problem that might have been solved by the use of several
         other commands.

         The points definition commands are

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~  ~~  ~~~~~~~~~~~~~~~~~~~~~~~
         82  Tangent                   42  Fit Curve
         83  Tangent Offset            59  Parallel Figure
         32  Divide Arc                60  Parallel Line
         33  Divide Figure             80  Streets Intersect
         34  Divide Line



                      LINE & CURVE INTERSECTION COMMANDS
                      ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

         These commands will compute the intersections of two lines, a
         line and a curve, two curves, a line and a figure, a curve
         and a figure, or two figures.  Each time one of these
         commands is invoked, a single point of intersection is
         computed.  If more than one intersection is possible, as in
         the case of intersecting a line with a curve, COGO will
         compute all possible intersections and YOU must select the
         correct intersection by specifying its proximity (nearest or
         farthest) to a pre-selected point of YOUR specification
         (usually designated as "M" in the variable data lists).

         In all of these commands which utilize figures or straight
         lines, you must consider the lines to be extended to infinity
         at each of their ends.

         The line and curve intersection commands are:

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~  ~~  ~~~~~~~~~~~~~~~~~~~~~~~
         12  Azimuth Intersect          7  Arc Line Bearing
         18  Bearing Intersect          8  Arc Line Points
         63  Points Intersect           5  Arc Arc Intersect
         61  Points Azimuth Intersect  38  Figure Arc Intersect
         62  Points Bearing Intersect  39  Figure Figure Intersect
          6  Arc Line Azimuth          40  Figure Line Intersect










          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  36

                             DATA DISPLAY COMMANDS
                             ~~~~~~~~~~~~~~~~~~~~~

         Although these commands do compute values, they neither store
         nor modify data but rather display it.

         The data display commands are:

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~  ~~  ~~~~~~~~~~~~~~~~~~~~~~~
         48  List Coordinates          84  Traverse Angles
         49  List Figures              85  Traverse Azimuths
         31  Distance                  86  Traverse Bearings
         45  Inverse Azimuths          87  Traverse Deflections
         46  Inverse Bearings           4  Angles
          9  Area                      66  Segment
         10  Area Azimuths             67  Segment Plus
         11  Area Bearings             68  Segment Minus



                           FIGURE ALIGNENT COMMANDS
                           ~~~~~~~~~~~~~~~~~~~~~~~~

         These commands provide the capability of working with an
         entire alignment, including any number of straight lines and
         circular curves.

         In each of the commands, the alignment to be used is
         specified by the first 3 data variables.

         The 1st item is the figure number or description to be used
         as the alignment, which must be described in ASCENDING order
         of stationing (the 2nd point in DESC must have a higher value
         than the 1st).  If this is NOT the case, then TRANSPOSE the
         description by appending the letter "T" to the DESC.

         The 2nd item is the point number of the point to be used to
         define the stationing, which may be ANY point.

         The 3rd item is the station of the above-mentioned point.

         NOTE: These commands consider the alignment to be extended
               along a tangent of each end when stations are outside
               the range of the specified alignment.

         The figure alignment commands are:

                          #  NAME
                         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~
                         75  Stations And Offsets
                         64  Points On Alignment
                         55  Locate From Alignment
                          3  Alignment Offset
                         29  Describe Alignment Azimuths
                         30  Describe Alignment Bearings


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  37

                                SPIRAL COMMANDS
                                ~~~~~~~~~~~~~~~

         These commands augument the preceding FIGURE ALIGNMENT
         COMMANDS by introducing spirals to the alignments; in all of
         the following commands, the alignments contain spirals.

         Several of the commands refer to "spiral in" and "spiral
         out".  Transitioning from a straight line to a circle is the
         spiral in (also known as tangent-to-spiral), and
         transitioning from the circle to a straight line is the
         spiral out (also known as spiral-to-tangent).

         The spiral commands are:

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~  ~~  ~~~~~~~~~~~~~~~~~~~~~~~
         70  Simple Spiral             47  Line Spiral
         71  Spiral Length             19  Compound Spiral
         72  Spiral Offset             73  Spiral Spiral
         23  Coordinate POSP           25  Curve Spiral
                                       41  Fit Alignment



                              ALIGNMENT COMMANDS
                              ~~~~~~~~~~~~~~~~~~

         These commands are used to define and solve the geometry
         associated with alignments, including simple curves,
         tangents, offsets, and stationing along the line.  All curves
         are circular and stations are expressed in decimal feet
         (STAtion 23+34.546 is entered as 2334.546).

         Note that an ALIGNMENT or DEFINE CURVE command must preceed:

                  COORDINATE POA      COORDINATE OFFSET
                  OFFSET ALIGNMENT    STATION FROM COORDINATE

         The ALIGNMENT or DEFINE CURVE commands establishes a circular
         curve in memory by storing its parameters (only 1 set at a
         time).  The above commands then will apply to that curve.  If
         a 2nd ALIGNMENT or DEFINE CURVE command is given, a new curve
         is established, the above commands refer to the new curve,
         and the 1st curve no longer exists.  Any curve established
         and defined will remain in memory until a new curve is
         defined.  If all of the curve data is known, use the DEFINE
         CURVE command to establish the curve in memory; if the curve
         has unknown values, use the ALIGNMENT command.

          #  NAME                       #  NAME
         ~~  ~~~~~~~~~~~~~~~~~~~~~~~~  ~~  ~~~~~~~~~~~~~~~~~~~~~~~
          2  Alignment                 21  Coordinate Offset
         26  Define Curve              76  Stations From Coordinates
         22  Coordinate POA            57  Offset Alignment



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  38

                            COMMAND VARIABLE NAMES


         The input variables used by the various commands are
         explained below; every effort was made to keep the variable
         names as simple and as logical as possible.  All input
         variables must conform to the sequencing that is specified in
         the command descriptions on the following pages.

         VARIABLE  GENERAL DESCRIPTION
         ~~~~~~~~  ~~~~~~~~~~~~~~~~~~~
         I         A point # of an Intersection - usually sought.
         PC        A point # of a Point of Curvature.
         PT        A point # of a Point of Tangency.
         PI        A point # of a Point of Intersection.
         BS        A point # to be used as a BackSight.
         BT        A point # of a point on Back Tangent.
         FS        A point # to be used as a ForeSight.
         FT        A point # of a point on Foreward Tangent.
         POA       A point # of a Point On Arc.
         V         A point # of a circle's Vertex or an angle point.
         L         A point # that begins sequential assignment.
         BEGIN     A point # that begins a figure or alignment.
         END       A point # that ends a figure or alignment.
         N, J, K   A point # - usually specified in the description.
         X         Value to be specified - usually a distance.
         R         Value of an arc's Radius.
         A         Value of a specified Azimuth.
         B         Value of a specified Bearing.
         G         Value of a specified anGle.
         CA        Value of a specified Central Angle of a curve.
         DCA       Value of a specified Deg of Curve (Arc Definition).
         S, STA    Value of a Station (STA 1234+12.123)
         DS        Value dividing a line/arc into equal segments.
         F         A figure #.
         DESC      A figure DESCription - either sequential point #'s,
                                          or, a figure #.
         /         End of Data marker   - any variables after this
                                          marker are optional but are
                                          not to be typed.
         CRV       A CuRVe number - between 1 and 999.
         M         A reference - generally for intersections; make the
                                 intersect closest to +M or farthest
                                 from -M.

                                 ABBREVIATIONS
                                 ~~~~~~~~~~~~~
         All commands may be abbreviated, provided:

         1) The first letter of each command word must be used in the
            abbreviation (i.e. [I]nverse [B]earing = I B).
         2) Enough letters of the command are used in the remainder
            of the abbreviation to differentiate it from other
            commands.  For example, DE C can not be used because
            commands [DE]fine [C]urve and [DE]lete [C]oordinates share
            the same abbreviation.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  39

                                  ADJUST AREA


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           1  AD AR        DESC  AREA  BEGIN  END  N  J  /  ALSO


         Adjust the area described by DESC to be AREA in square feet.
         Make the adjustment in the sides starting at point BEGIN and
         ending at point END.  Variables N and J are additional
         parameters needed by some methods.  Points described in ALSO,
         although not part of DESC, will be moved in the same manner
         as the points between BEGIN and END.


         NOTE: None of the points to be adjusted may be the 1st or
               last point in the figure description.

         NOTE: BEGIN and END must be specified in the same sequence
               that they appear in the description DESC.

         NOTE: This is an extremely powerful command that may
               otherwise be known as AREA CUT-OFF.


         OUTPUT: The initial and final areas are expressed in square
                 feet.  Coordinates are changed to reflect the new
                 area.


         ROTATIONAL Rotate the sides between BEGIN and END about point
         METHOD #1  N, where N may be any defined point.  J is not
           (J=0)    used but it must be entered as 0 to satisfy input
                    format requirements.

         PERPEN-    Move the sides between BEGIN and END in a
         DICULAR    direction perpendicular to a line connecting
         METHOD #2  points BEGIN and END.  Points N and J are not used
           (N=0,    but must be entered as 0 to satisfy input format
            J=0)    requirements.

         PARALLEL   Move the sides between BEGIN and END in a
         METHOD #3  direction parallel to a line connecting points N
                    and J.


         CAUTION: Present coordinates may be used to create new
                  coordinates, erasing old values.  These old values,
                  once written over by the new values, can not be
                  recovered - exercise caution !!!

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  40

                                   ALIGNMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           2  ALI          CRV  BT  PI  FT  PC  V  PT  R  TAN  SBT  X


         ALIGNMENT is used to define and solve the geometry of
         circular curves, defining any given curve as number CRV.
         Adjoining curves can then be identified and used by their CRV
         numbers.

         CRV - Identification number assigned to CuRVe (0 to 999).
         BT  - Any known point on Back Tangent.
         PI  - Known Point Of Intersection of the tangents.
         FT  - Any known point on Foreward Tangent.
         PC  - Number assigned to the Point of Curvature.
         V   - Number assigned to the Vertex of the curve.
         PT  - Number assigned to the Point of Tangency.
         R   - Radius of curve (if unknown = 0).
         TAN - Length of curve Tangent (if unknown = 0).
         SBT - The Station of previously entered point BT.  If this
               value is entered as -1, point BT is considered (and
               must be entered as) the PT of previous curve; also, SBT
               is assumed to be the station of the previous PT (that
               is, X = 0).  This allows stationing to be automatically
               carried foreward.
         X   - Fixed distance from BT to PC.  If V and TAN are unknown
               (0 must be input) and X = 0, the curve will be
               compounded or reversed with the previous curve.  If V
               and TAN are unknown (0 must be input) and X has a value
               such as X = 150', the curve will be computed such that
               the PC is 150' from the BT (usually, but not
               necessarily, the PT of the previous curve.)

         NOTE: All PI's must have been prevously located.

         NOTE: IF X=0, TAN=0, and V=0, then the BT must be the same
               point number as the PC.

         NOTE: Stationing is input as decimal feet (STA 23+21 = 2321.)

         NOTE: Where a distance or length is unknown, the value 0 must
               be entered; operators cannot be used in the command.

         NOTE: The ALIGNMENT command must preceed the following
               commands:
                             COORDINATE POINT ON ARC
                             COORDINATE OFFSET
                             STATION FROM COORDINATE
                             OFFSET ALIGNMENT






          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  41

                               ALIGNMENT OFFSET


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           3  A OF         DESC  N  STAN  J  K


         This command is used to locate a point on an alignment from
         an offset point.  DESC is either a figure number or
         description.  Stationing is defined by point N having station
         S.  Point J is located on the alignment by drawing a
         perpendicular from point K to the alignment.


         EXAMPLE: A OF (1 2 C3R 4) 2 10560 10 50


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.





































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  42

                                    ANGLES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           4  ANG          DESC


         In the figure described by DESC, compute:

            1) The distance from back point B to angle point A
            2) The clockwise angle from back point B to foreward point
               F as observed at angle point A
            3) The distance from angle point A to foreward point F.



         EXAMPLE: ANGLES 5 (using a figure number)

                         B   A   F   B/A DIST  B/A/F ANGLE  A/F DIST
                        --- --- ---  --------  -----------  --------
                  ANGLE 834 674 462  347.4598  177 21 34.4  467.2387
                  ANGLE 674 462 355  467.2387   67 14 13.0  388.8801
                  ANGLE 462 355 901  388.8801  204 15 23.4   78.3116
                  etc..........



         EXAMPLE: ANGLES 674 462 355 (using coordinate point numbers)

                         B   A   F   B/A DIST  B/A/F ANGLE  A/F DIST
                        --- --- ---  --------  -----------  --------
                  ANGLE 674 462 355  467.2387   67 14 13.0  388.8801


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.




















          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  43

                               ARC ARC INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           5  A A I        I  V1 R1  V2 R2  M


         Locate point I by intersectng the circle centered at V1
         having radius R1, with the circle centered at V2 having
         radius R2.

         This particular command is also known, in other COGO's, as
         "DISTANCE/DISTANCE INTERSECT".  If you are used to calling it
         by that name, simply consider the two distances as R1 and
         R2.


         NOTE: The desired intersection will be the one closest to
               positive point M, or farthest from negative point M.






































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  44

                               ARC LINE AZIMUTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           6  A L A        I  V R  P A  M  /  OFF


         Locate point I by intersecting a circle whose vertex is at V
         and whose radius is R, with the line through point P on an
         azimuth (or optionally, a bearing) of A.

         This particular command is also known, in other COGO's, as
         "AZIMUTH/DISTANCE INTERSECT".  If you are used to calling it
         by that name, simply consider the distance as R.


         NOTE: The desired intersection will be the one closest to
               positive point M, or farthest from negative point M.

         NOTE: OFF is the optional offset distance from the line
               through P.




































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  45

                               ARC LINE BEARING


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           7  A L B        I  V R  P B  M  /  OFF


         Locate point I by intersecting a circle whose vertex is at V
         and whose radius is R, with the line through point P on a
         bearing (or optionally, an azimuth) of B.

         This particular command is also known, in other COGO's, as
         "BEARING/DISTANCE INTERSECT".  If you are used to calling it
         by that name, simply consider the distance as R.


         NOTE: The desired intersection will be the one closest to
               positive point M, or farthest from negative point M.

         NOTE: OFF is the optional offset distance from the line
               through P.




































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  46

                                ARC LINE POINTS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           8  A L P        I  V R  P N  M  /  OFF


         Locate point I by intersecting a circle whose vertex is at
         point V and whose radius is R, with the line defined by
         points P and N.



         NOTE: The desired intersection will be the one closest to
               positive point M, or farthest from negative point M.

         NOTE: OFF is the optional offset distance from the line
               through points P and N.







































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  47

                                     AREA


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           9  AR           DESC


         Compute and display the area enclosed by the points of
         description DESC.  The last point number must be the same as
         the first.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.










































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  48

                                 AREA AZIMUTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          10  AR A         DESC


         Compute and display the area enclosed by the points of
         description DESC.  Also, for each line, compute and display
         the course distance and azimuth.  The last point number must
         be the same as the first.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.









































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  49

                                 AREA BEARING


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          11  AR B         DESC


         Compute and display the area enclosed by the points of
         description DESC.  Also, for each line, compute and display
         the course distance and bearing.  The last point number must
         be the same as the first.

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.










































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  50

                               AZIMUTH INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          12  A I          I  J A1  K A2  /  OFFA  /  OFFB


         Locate point I by intersecting the line through point J at
         azimuth A1 with the line through K at azimuth A2.

         This particular command is also known, in other COGO's, as
         "AZIMUTH/AZIMUTH INTERSECT".



         NOTE: OFFA and OFFB are optional offsets.









































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  51

                                  BATCH PRINT

         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          16  BA PR        N

         Read an ASCII disk file and execute the input stream of
         commands to the printer.

         N =  0, Input  is sent to printer; output is sent to printer.
         N =  1, Input not sent to printer; output is sent to printer.
         N = -1, Only error messages will be sent to printer.

         When the input is ended, COGO resets to TYPE SCREEN status
         with the print control remaining as previously set and system
         is in pause status.

         This command is quite powerful when properly used.  For
         example, you may have one of your technicians (or secretary)
         type the following commands and field data using your WORD
         PROCESSING PROGRAM or TEXT EDITOR.  Note that all input
         commands and data are in UPPER CASE:

         TYPE PRINT                               --     This is
         KNOWN 1 10000 1000                         |    created on
         LOCATE BEARING 1 2 N 45 00 00 E 1000.000   |    your word
         LOCATE BEARING 2 3 S 44 00 00 E 1000.000   |->  processor &
         LOCATE BEARING 3 4 S 45 00 00 W 1000.000   |    named
         LOCATE BEARING 4 5 N 45 00 00 W 1000.000   |    YOURFILE.INP
         END OF JOB                               -

         After "batching" this in, suppose you find that it doesn't
         close.  Rather than finding the blunder and correcting all
         courses from that point, interactively from the keyboard, all
         you have to do is correct that ONE course (in the word
         processor) and re-batch it back in COGO.  When only 10 or 20
         courses are involved, interactive keyboard input is simple
         and efficient; when many more courses must be entered, the
         BATCH input method is much more effective and allows easier
         correction of input errors.

         NOTE: Any text file (ASCII) must be labeled with an extension
               of [.INP].  The full input command might be:

               BATCH PRINT -1          (type the command - no output)
               input file?             (COGO asks for the .INP file)
               YOURFILE                (you enter the .INP filename
                                        WITHOUT the .INP extension)

               Where YOURFILE.INP contains the commands and field
               data listed above.

         Unless you require a printed record of the input/output
         during the batch computations, we suggest you specify the -1
         switch of no output.  This will speed the batch process
         considerably.  See the SAMPLE PROBLEM for more details.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  52

                                 BATCH SCREEN

         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          17  BA SC        N

         Read an ASCII disk file and execute the input stream of
         commands to the monitor screen.

         N =  0, Input  is sent to screen; output is sent to screen.
         N =  1, Input not sent to screen; output is sent to screen.
         N = -1, Only error messages will be sent to screen.

         When the input is ended, COGO resets to TYPE SCREEN status
         with the print control remaining as previously set and system
         is in pause status.

         This command is quite powerful when properly used.  For
         example, you may have one of your technicians (or secretary)
         type the following commands and field data using your WORD
         PROCESSING PROGRAM or TEXT EDITOR.  Note that all input
         commands and data are in UPPER CASE:

         TYPE PRINT                               --     This is
         KNOWN 1 10000 1000                         |    created on
         LOCATE BEARING 1 2 N 45 00 00 E 1000.000   |    your word
         LOCATE BEARING 2 3 S 44 00 00 E 1000.000   |->  processor &
         LOCATE BEARING 3 4 S 45 00 00 W 1000.000   |    named
         LOCATE BEARING 4 5 N 45 00 00 W 1000.000   |    YOURFILE.INP
         END OF JOB                               -

         After "batching" this in, suppose you find that it doesn't
         close.  Rather than finding the blunder and correcting all
         courses from that point, interactively from the keyboard, all
         you have to do is correct that ONE course (in the word
         processor) and re-batch it back in COGO.  When only 10 or 20
         courses are involved, interactive keyboard input is simple
         and efficient; when many more courses must be entered, the
         BATCH input method is much more effective and allows easier
         correction of input errors.

         NOTE: Any text file (ASCII) must be labeled with an extension
               of [.INP].  The full input command might be:

               BATCH SCREEN -1         (type the command - no output)
               input file?             (COGO asks for the .INP file)
               YOURFILE                (you enter the .INP filename
                                        WITHOUT the .INP extension)

               Where YOURFILE.INP contains the commands and field
               data listed above.

         Unless you require a printed record of the input/output
         during the batch computations, we suggest you specify the -1
         switch of no output.  This will speed the patch process
         considerably.  See the SAMPLE PROBLEM for more details.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  53

                               BEARING INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          18  B I          I  J B1  K B2  /  OFFA  /  OFFB


         Locate point I by intersecting the line through point J at
         bearing B1 with the line through K at bearing B2.

         This particular command is also known, in other COGO's, as
         "BEARING/BEARING INTERSECT".



         NOTE: OFFA and OFFB are optional offsets.









































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  54

                                COMPOUND SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          19  CO S         CRV  BT CS  PI SC  X  DC1 DC2  SGN


         Calculate the compound curve, given the following:

         CRV = Assigned CuRVe identification number (1-999).
         BT  = Known point on the Back Tangent.
         CS  = Known point on the point of change of Curve to Spiral.
         PI  = Assigned Point of Intersection of the two tangents.
         SC  = Assigned point of point of change of Spiral to Curve.
         X   = Known length of compound spiral, meas. from CS to SC.
         DC1 = Degree of Curve of circular curve 1 (the central angle
               which subtends a 100 foot arc) in DEG-MIN-SEC format.
         DC2 = Degree of Curve of circular curve 2 (the central angle
               which subtends a 100 foot arc) in DEG-MIN-SEC format.
         SGN = 1 for clockwise curve, -1 for counterclockwise curve.


         OUTPUT: Curve number
                 Coordinates of CS
                 Coordinates of PI
                 Coordinates of SC
                 Tangent lengths
                 Tangent azimuths





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  55

                               CONVERT MERIDIAN


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          20  C M          DESCJ DESCK  J K  G  /  SCALE


         Rotate and translate the known coordinates of description
         DESCJ, storing the resulting values in the points of
         description DESCK.  Point J is a point in the original system
         and point K is the corresponding point in the converted
         system.  G is the angle of rotation.  If points J and K are
         descriptions DESCJ and DESCK, then they will be used to tie
         the descriptions together; otherwise, the figures will be
         tied by their first points.  Distances between all points in
         the figure are multiplied by the optional SCALE.

         For example, if J is the 5th point of DESCJ and K is the 8th
         point of DESCK, then the 6th point of DESCJ will be converted
         and stored in the 9th point of DESCK, the 7th in the 10th,
         etc.  When the end of either figure is reached, the 1st point
         will be next until all points in DESCJ have been converted.
         If a point number appears more than once in DESCJ, it will be
         converted only once.  Description DESCK must be as large as,
         or larger, than DESCJ.  If it is not desired to save the old
         coordinates, DESCK may equal DESCJ.


         CAUTION: Present coordinates may be used to create new
                  coordinates, erasing old values.  These old values,
                  once written over by the new values, can not be
                  recovered - exercise caution !!!


         DESCK OR DESKJ may take the form of a figure number, or, a
         series of coordinate point numbers - (#xxx #xxx #xxx...#xxx).
         It is suggested that wherever possible, put the points in a
         figure.



















          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  56

                               COORDINATE OFFSET


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          21  C O          J  S  X


         Compute the coordinates of point J, along an arc station S,
         and radially offset from the arc by the distance X.  If
         offset point J is to the left of the arc (along stationing)
         assign a negative sign to X; if J is to the right, it is
         positive.

         Note that the curve must have been previously defined by a
         DEFINE CURVE or ALIGNMENT command.










































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  57

                            COORDINATE POINT ON ARC


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          22  C POA        J  S


         Compute the coordinates of assigned point on arc J, whose arc
         station is S.

         Note that the curve must have been previously defined by a
         DEFINE CURVE or ALIGNMENT command.













































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  58

                          COORDINATE POINT ON SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          23  C POS        J  X


         Locate point J on a previously defined SIMPLE SPIRAL or
         SPIRAL LENGTH the distance X from the "Tangent-To-Spiral" as
         measured along the curve.

         OUTPUT: Point #N and its coordinates; the spiral number, the
                 length along the spiral, and the azimuth of the
                 tangent at point N.











































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  59

                                   COPY FILE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          24  CO FI        FILE1  FILE2


         Copies the contents of FILE1 into file FILE2, on the same
         disk, so long as FILE2 does not already exist.

         This command can be found convenient when you wish to attempt
         trial computations or just experiment with an existing but do
         not want to permanently alter the file.  COPY FILE thus
         allows you to create a second, identical file with which to
         experiment so that the original file is not altered.










































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  60

                                 CURVE SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          25  CV S         I  R V  M


         Compute the intersection point I of the spiral previously
         defined by SIMPLE SPIRAL or SPIRAL LENGTH, and the circular
         curve defined by vertex V and radius R.  If two intersections
         are found, point I will be computed closest to point M.

         OUTPUT: Coordinates of point I.
                 Distance from "Tangent-To-Spiral" to point I.











































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  61

                                 DEFINE CURVE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          26  DEF C        CRV  PC SPC  PI  PT SPT  V  SIGN


         Define a curve so that future commands will be recognized;
         the  DEFINE CURVE  command itself outputs no data.


         CRV   =  Number to be assigned to the CURVe (1-999)
         PC    =  Number to be assigned to the Point of Curvature.
         SPC   =  Known Station value to be assigned to the PC.
         PI    =  Known Number of Point of Intersection of tangents.
         PT    =  Known Number of Point of Tangency.
         SPT   =  Known Station value to be assigned to the PT.
         V     =  Known Number of the Vertex of the curve.
         SIGN  =  1.0 for clockwise; -1.0 for counterclockwise.


         This command should precede many other commands that require
         a curve to have been previously defined, such as:

                       21  Coordinate Offset
                       22  Coordinate Point On Arc (POA)
                       57  Offset Alignment
                       75  Station And Offset





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  62

                              DELETE COORDINATES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          27  DEL C        DESC


         Deletes coordinates from disk memory.


         DESC = Figure number or specified points.


         EXAMPLES: DEL C (5)         Delete coords of Point 5
                   DEL C 5           Delete coords of Figure 5
                   DEL C (1 5 10)    Delete coords of Points 1, 5, 10
                   DEL C (1-9999)    Delete ALL coords.


                 --------------------------------------------
                |                                            |
                |    EXERCISE CAUTION WITH THIS COMMAND!!!   |
                |                                            |
                |        ONCE YOU HAVE DELETED VALUES,       |
                |                                            |
                |          THEY CANNOT BE RECOVERED          |
                |                                            |
                 --------------------------------------------


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.
























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  63

                                DELETE FIGURES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          28  DEL F        DESC


         Deletes the figures specified in DESC from disk.


         EXAMPLES: STO F 3 (1-27)
                   DEL F 3         Delete figures 1 through 27.
                   DEL F 8         Delete figure 8.
                   DEL F (1-18)    Delete figures 1 through 18.



                 --------------------------------------------
                |                                            |
                |    EXERCISE CAUTION WITH THIS COMMAND!!!   |
                |                                            |
                |        ONCE YOU HAVE DELETED VALUES,       |
                |                                            |
                |          THEY CANNOT BE RECOVERED.         |
                |                                            |
                 --------------------------------------------



         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.

























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  64

                          DESCRIBE ALIGNMENT AZIMUTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          29  D A A        DESC  J  SJ  /  DS  /  FR  TO


         Describe (list) the alignment specified by DESC.


         DESC = Figure number or points description of alignment.
         J    = Any known point - used to define the stationing.
         SJ   = Known Station value of point J.
         DS   = If specified, compute/print coords & station for every
                point having a station evenly divisible by DS.
         FR   = If specified, describe alignment only FRom point FR.
         TO   = If specified, describe alignment only TO   point TO.


         OUTPUT: Coordinates and stations of all PC's, PT's, PI's;
                 coordinates of vertexes; azimuths of all tangents;
                 deflection angles at all PI's; and curve data such as
                 radii, degree of curve, tangent lengths, arc lengths,
                 externals, etc.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.




























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  65

                          DESCRIBE ALIGNMENT BEARINGS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          30  D A B        DESC  J  SJ  /  DS  /  FR  TO


         Describe (list) the alignment specified by DESC.


         DESC = Figure number or points description of alignment.
         J    = Any known point - used to define the stationing.
         SJ   = Known Station value of point J.
         DS   = If specified, compute/print coords & station for every
                point having a station evenly divisible by DS.
         FR   = If specified, describe alignment only FRom point FR.
         TO   = If specified, describe alignment only TO   point TO.


         OUTPUT: Coordinates and stations of all PC's, PT's, PI's;
                 coordinates of vertexes; bearings of all tangents;
                 deflection angles at all PI's; and curve data such as
                 radii, degree of curve, tangent lengths, arc lengths,
                 externals, etc.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.




























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  66

                                   DISTANCE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          31  DIS          DESC


         Compute the distances between points described in DESC.


         OUTPUT: Distance from 1st to 2nd points, 2nd to 3rd, 3rd to
                 4th, etc.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  67

                                  DIVIDE ARC


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          32  DIV A        J  K  V  DS  /  L


         Divide an arc whose vertex is at V, clockwise, from point J
         to point K, into DS equal parts.  Assign point numbers on the
         arc sequentially increasing from point L, if specified; if L
         is not specified, assign point numbers on the arc
         sequentially increasing from point J.


         EXAMPLE: DIV A 200 300 150 4


         OUTPUT:  PT#  NORTHING EASTING
                  ~~~  ~~~~~~~~ ~~~~~~~~
                  201   923.87   382.68
                  202   707.11   707.11
                  203   382.68   923.87



































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  68

                                 DIVIDE FIGURE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          33  DIV F        DESC  DS  L


         Divide the figure described by DESC into DS parts.  Store the
         resulting points as sequentially increasing point numbers
         beginning with L.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.










































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  69

                                  DIVIDE LINE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          34  DIV L        J  K  DS  /  L


         Divide a line beginning with point J and ending with point K
         into DS parts.  At each even division, assign point numbers
         on the line sequentially increasing from point L, if
         specified; if L is not specified, assign point numbers on the
         line sequentially increasing from point J.













































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  70

                                  END OF JOB


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          35  E O J        (none)


         At the completion of a job, this command updates the
         coordinate and figure files (saves all values to disk).  It
         MUST be used to end a job before beginning another.  It will
         not exit you from COGO, but does re-initialize the COGO
         program and resets all variables and arrays; in effect, you
         are in "start-up" mode to begin a new job.


         ************************************************************
         *                                                          *
         *                                                          *
         *          ALWAYS USE THIS COMMAND TO END ONE JOB          *
         *                                                          *
         *                 BEFORE BEGINNING ANOTHER                 *
         *                                                          *
         *                            OR                            *
         *                                                          *
         *             YOU WILL LOOSE YOUR COORDINATES              *
         *                                                          *
         *                                                          *
         ************************************************************





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  71

                                  END OF RUN


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          36  E O R        (none)


         Allows a "clean" exit to DOS from COGO.  It is identical in
         function to the END OF JOB command (updates disk files),
         except that instead of re-starting COGO, you are exited to
         the Disk Operating System of your PC.


         ************************************************************
         *                                                          *
         *                                                          *
         *               ALWAYS USE THIS COMMAND TO END             *
         *               ~~~~~~                                     *
         *                       A COGO SESSION                     *
         *                                                          *
         *                             -                            *
         *                                                          *
         *          IT SAVES YOUR COMPUTED VALUES TO DISK!          *
         *                                                          *
         *              IT RESETS YOUR [CAPSLOCK] KEYS!             *
         *                                                          *
         *                                                          *
         ************************************************************





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  72

                                  EXTEND ARC


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          37  E A          J  V  I  X


         From point J, extend an arc centered at vertex V, to locate
         point I, at arc length X.  Positive X extends clockwise;
         negative X extends counterclockwise.















































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  73

                             FIGURE ARC INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          38  F A I        I  F  V R  M  /  OFF


         Locate point I by intersecting any line in figure F with a
         circle whose vertex is at V and having a radius of R.  The
         intersection will be the one closest to positive point +M, or
         farthest from negative point -M.

         The intersection can be made with a line parallel to figure F
         (a "range line" of the figure's perimeter) by specifying an
         offset (range) distance OFF.


         CAUTION: The lines of the figure are extended to infinity,
                  which may allow MANY possible intersections.






































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  74

                            FIGURE FIGURE INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          39  F F I        I  F1  F2  M  /  OFF1  /  OFF2


         Locate point I by intersecting one figure F1 with another F2
         at a point closest to positive +M.  You may also intersect a
         range of F1 by specifying the offset distance OFF1; likewise
         with F2.


         CAUTION: Both ends of both figures extend to infinity.











































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  75

                             FIGURE LINE INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          40  F L I        I  F  J A  M  /  OFF  /  OFJ


         Locate point I by intersecting any line in figure F with a
         line through point J whose azimuth is A.  The intersection
         will be the one closest to positive point +M, or farthest
         from negative point -M.

         The intersection can be made with a line parallel to figure F
         (a "range line" of the figure's perimeter) by specifying an
         offset (range) distance OFF.

         The intersection can be made with a line parallel to line J
         (a "range line" of the J line) by specifying an
         offset (range) distance OFJ.


         CAUTION: The ends of the figure extend to infinity.



































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  76

                                 FIT ALIGNMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          41  F A          CRV  BT  PI  DCA  XS1  XS2  G  SIGN


         Compute an alignment.


         CRV  = Alignment ID number (1-999) to be assigned.
         BT   = Known point on Back Tangent.
         PI   = Known point at Point of Intersection of tangents,
         DCA  = Degree of Curvature (Arc Definition).
         XS1  = Length of 1st Spiral (from TS to SC).
         XS2  = Length of 2nd Spiral (from SC to ST).
         G    = Deflection angle of tangents (must show the minutes
                and seconds - i.e. 23 00 00, even if they're null).
         SIGN = +1.0 is clockwise; -1.0 is counterclockwise.


         NOTE:  Points from CRV to CRV+S are used up by this command;
                pre-existing points in this range will be destroyed.


































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  77

                                   FIT CURVE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          42  F C          BT PI FT  PC V PT  /  R


         Fit a curve.


         BT = Known point on Back Tangent.
         PI = Known Point of Intersection of tangents.
         FT = Known point on Foreward Tangent.
         PC = Assign point number to intended Point of Curvature.
         V  = Assign point number to intended Vertex of curve.
         PT = Assign point number to intended Point of Tangency.
         R  = Known Radius of curve.


         NOTE: If BT=PC or FT=PT (or both), then R may be omitted.





































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  78

                                GET COORDINATES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          43  G C          NEWDESC  OLDDESC  OLDFILE


         Place into the points specified by the range NEWDESC the
         coordinates assigned to points specified by the range OLDDESC
         from the file OLDFILE, residing on the default disk drive.


         EXAMPLES: G C (7) (23) 145         Copy coords of pt. 23 in
                                            file 145 to pt. 7
                   STO FIG 10 (1-20)
                   G C 10 10 145            Copy coords of pts. 1 to
                                            20 in file 145 to points
                                            1 to 20.
                   STO FIG (2 4 26 49)
                   G C (8-10 7) 1 155       Copy coords of pts. 2, 4,
                                            26 and 49 in file 155 to
                                            points 8, 9, 10 and 7.


         NEWDESC OR OLDDESC may take the form of a figure number, or,
         a series of coordinate point numbers - (#xxx #xxx.....#xxx).
         It is suggested that wherever possible, put the points in a
         figure.





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  79

                                  GET FIGURES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          44  G F          NEWDESC  OLDDESC  OLDFILE


         Place into the figures specified by the range NEWDESC the
         figures specified by the range OLDDESC from the file OLDFILE
         residing on the default disk drive.


         EXAMPLES: G F (7) (23) 145         Copy figure 23 in file 145
                                            figure 7.
                   STO FIG 10 (1-20)
                   G F 10 10 145            Copy figures 1 to 10 in
                                            file 145 to figures 1 to
                                            20.
                   STO FIG (2 4 26 49)
                   G F (8-10 7) 1 155       Copy figures 2, 4, 26, and
                                            49 in file 155 to figures
                                            8, 9, 10 and 7.


         NEWDESC OR OLDDESC may take the form of a figure number, or,
         a series of coordinate point numbers - (#xxx #xxx.....#xxx).
         It is suggested that wherever possible, put the points in a
         figure.





























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  80

                                INVERSE AZIMUTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          45  I A          DESC


         Inverse between points specified by DESC.


         OUTPUT: Point numbers \    (sequentially from
                 Azimuths       >        first to last points
                 Distances     /             defined by DESC).


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.







































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  81

                                INVERSE BEARING


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          46  I B          DESC


         Inverse between points specified by DESC.


         OUTPUT: Point numbers \    (sequentially from
                 Bearings       >        first to last points
                 Distances     /             defined by DESC).


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.







































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  82

                                  LINE SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          47  L S          I  J  K  M


         Find the Intersection point I of a line defined by points J
         and K, with a spiral curve previously defined by SIMPLE
         SPIRAL or SPIRAL LENGTH.

         If two intersections exist, the intersection I will be
         assigned to the point closest to positive point M.












































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  83

                               LIST COORDINATES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          48  L C          DESC


         All points and coordinates in the range specified by DESC are
         listed, except those points that are undefined.


         EXAMPLES: L C 1-10            List points 1 to 10.
                   L C (12)            List point 12.
                   L C 15              List points in figure 15.
                   L C (1-4, 6-9)      List points 1 to 4 and 6 to 9.


         To reduce disk access times, try to keep the range of
         coordinate point numbers as narrow as possible.  If you only
         need to view points 40 to 85, then specify LIST COORDS 40-85,
         not 1-300.  Also, use range specifiers whenever possible,
         such as LIST COORDS (1-4 6-9) instead of (1 2 3 4 6 7 8 9).


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.






























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  84

                                 LIST FIGURES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          49  L FIG        DESC


         All figures in the range specified by DESC are listed, except
         those figures that are undefined.


         EXAMPLES: L F (1 10)          List figures 1 and 10.
                   L F (12)            List figure 12.
                   L F 15              List figures in figure 15.
                   L F (1-4 6-9)       List figures 1 to 4 and 6 to 9.


         To reduce disk access times, try to keep the range of figure
         numbers as narrow as possible.  If you only need to view
         figures 4 to 8, then specify LIST FIGURES (4-8), not 1-30.
         Also, use range specifiers whenever possible, such as LIST
         FIGURES (1-3 7-9) instead of (1 2 3 7 8 9).


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.






























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  85

                                  LIST FILES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          50  L FILE       DESC


         Lists the COGO files on the default disk drive as specified
         by DESC, which must be in the range 1 to 999.


         To reduce disk access times, try to keep the range of file
         numbers as narrow as possible.  If you only need to view
         files 4 to 8, then specify LIST FILES (4-8), not 1-30.
         Also, use range specifiers whenever possible, such as LIST
         FILES (1-3 7-9) instead of (1 2 3 7 8 9).









































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  86

                                 LOCATE ANGLE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          51  L AG         BS  V  FS  A  X  /  G


         Backsight on BS, turn angle A at point V to locate point FS
         the distance X from point V.

         Angle G is an optional vertical angle if X is a slope
         distance.  The nearest multiple of 90 degrees will be taken
         as horizontal so that vertical angles measured from horizon,
         zenith, or nadir may be used.

         If a negative distance is used, the vector is backwards as
         if 180 degrees were added to the specified angle A.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  87

                                LOCATE AZIMUTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          52  L AZ         BS  FS  A  X  /  G


         From point BS, locate point FS the distance X and along
         azimuth A.

         Angle G is an optional vertical angle if X is a slope
         distance.  The nearest multiple of 90 degrees will be taken
         as horizontal so that vertical angles measured from horizon,
         zenith, or nadir may be used.

         If a negative distance is used, the vector is backwards as
         if 180 degrees were added to the specified azimuth A.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  88

                                LOCATE BEARING


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          53  L BR         BS  FS  B  X  /  G


         From point BS, locate point FS the distance X and along
         bearing B.

         Angle G is an optional vertical angle if X is a slope
         distance.  The nearest multiple of 90 degrees will be taken
         as horizontal so that vertical angles measured from horizon,
         zenith, or nadir may be used.

         If a negative distance is used, the vector is backwards as
         if the reverse of the specified bearing B was used.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  89

                               LOCATE DEFLECTION


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          54  L DE         BS  V  FS  D  X  /  G


         Backsight on point BS, turn deflection angle D at point V to
         locate point FS.

         Angle G is an optional vertical angle if X is a slope
         distance.  The nearest multiple of 90 degrees will be taken
         as horizontal so that vertical angles measured from horizon,
         zenith, or nadir may be used.

         If a negative distance is used, the vector is backwards as
         if 180 degrees were added to the specified deflection angle
         D.







































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  90

                             LOCATE FROM ALIGNMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          55  L F A        DESC  J SJ  N SN  /  OFFN


         Compute location of point N from an alignment.  The alignment
         is specified by figure number or description DESC with
         stationing defined by J having station SJ.  Point N is
         located from the alignment at station SN and optional OFFset
         OFFN.


         EXAMPLES: L F A (1-5) 2 642.5 11 637
                   STO FIG 1 (1-5)
                   L F A 1 2 642.5 11 637
                   L F A (1 2 C3R 4) 2 10560 10 10572


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.


































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  91

                                  LOCATE LINE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          56  L L          BS  FS  I  X  /  G


         From point BS in the direction of point FS, locate point I
         the distance X.

         Angle G is an optional vertical angle if X is a slope
         distance.  The nearest multiple of 90 degrees will be taken
         as horizontal so that vertical angles measured from horizon,
         zenith, or nadir may be used.

         If a negative distance is used, the vector is backwards as
         if the direction FS to BS (instead of the specified BS to FS)
         were used.







































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  92

                               OFFSET ALIGNMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          57  O A          I  J


         Locate point I (on arc) as the intersection, on a line
         projected from the vertex of a previously defined curve
         through any known point J.


         I = Point to be located by intersection, usually on arc (or,
             optionally, the back tangent).
         J = Any known point.


         NOTE: The curve must have been previously defined via the
               DEFINE CURVE or ALIGNMENT commands.

         NOTE: If a line projection FROM the vertex of the curve TO
               point J does not intersect the arc between its defined
               PC and PT, then the intersection will always occur on
               the back tangent line at a right angle to J.


         OUTPUT: I, J, station, offset (-offset if left), coords of I.






























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  93

                                PARALLEL FIGURE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          59  PAR F        F  OFF  L


         From the line described by figure F, locate the points of a
         line which is parallel by the offset distance OFF.  Assign
         point numbers as L, L+1, L+2, L+3, etc.

         The centers of curves are not defined by this command because
         they are the same as those of figure F.












































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  94

                                 PARALLEL LINE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          60  PAR L        BS1  FS1  OFF  BS2  FS2


         From the line defined by points BS1 to FS1, at the offset
         distance OFF (negative OFF if left, positive right), define a
         parallel line by locating points BS2 and FS2.















































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  95

                           POINTS AZIMUTH INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          61  P A I        I  J  K  BEGIN  A  /  OFF1  /  OFF2


         Find the intersection I by intersecting the line defined by
         points J and K, with a line beginning at point BEGIN whose
         azimuth is A.  Offsets OFF1 and OFF2 are optional.


         NOTE: Consider the ends of straight lines or figures to
               extend to infinity.











































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  96

                           POINTS BEARING INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          62  P B I        I  J  K  BEGIN  B  /  OFF1  /  OFF2


         Find the intersection I by intersecting the line defined by
         points J and K, with a line beginning at point BEGIN whose
         bearing is B.  Offsets OFF1 and OFF2 are optional.

         NOTE: Consider the ends of straight lines or figures to
               extend to infinity.












































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  97

                               POINTS INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          63  P I          I  J1 K1  J2 K2  /  OFF1  /  OFF2


         Find the intersection I by intersecting the line defined by
         points J1 and K1, with the line defined by points J2 and K2.
         Offsets OFF1 and OFF2 are optional.

         NOTE: Consider the ends of straight lines or figures to
               extend to infinity.












































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  98

                              POINTS ON ALIGNMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          64  P O A        DESC  J SJ  DS L  /  OFFJ  /  BEGIN  /  END


         Compute points at fixed intervals along an alignment which is
         specified by figure number or alignment (DESC).  Stationing
         is specified by point J whose station is SJ.  Points are
         computed along the alignment at each position that has a
         station evenly divisible by the interval DS in feet and
         optional offset OFFJ.  Computed points are stored in L, L+1,
         L+2, L+3, etc.  Optional BEGIN and END points may be
         specified as limits, beyond which no points will be computed.


         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.





































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page  99

                                   REDEFINE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          65  RED          J  K


         Assign the coordinates of point J to point K.  J is not
         disturbed.
















































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 100

                                    SEGMENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          66  SEG          POA1  POA2  R


         For the segment of a circle whose radius is R intersecting
         the arc at points POA1 and POA2, compute the segment area.

         OUTPUT: The chord length, arc length between POA1 and POA2,
                 and the segment area.













































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 101

                                     SEGMENT PLUS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          67  SEG P        POA1  POA2  R


         For the segment of a circle whose radius is R intersecting
         the arc at points POA1 and POA2, compute the segment area.


         OUTPUT: The chord length, arc length between POA1 and POA2,
                 and the segment area.


         NOTE: When SEGMENT PLUS (or SEGMENT MINUS) is used, the
               segment area is added (or subtracted) to the cumulative
               net area resulting from the last AREA type command and
               the previous SEGMENT PLUS (or SEGMENT MINUS) commands.
               This allows any number of segments to be added (or
               subtracted) to (from) a polygon bounded by multiple
               curves. After each SEGMENT PLUS (or SEGMENT MINUS), the
               area up to that point is displayed.


































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 102

                                 SEGMENT MINUS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          68  SEG M        POA1  POA2  R


         For the segment of a circle whose radius is R intersecting
         the arc at points POA1 and POA2, compute the segment area.


         OUTPUT: The chord length, arc length between POA1 and POA2,
                 and the segment area.


         NOTE: When SEGMENT MINUS (or SEGMENT PLUS) is used, the
               segment area is subtracted (or added) to the cumulative
               net area resulting from the last AREA type command and
               the previous SEGMENT MINUS (or SEGMENT PLUS) commands.
               This allows any number of segments to be subtracted (or
               added) from (to) a polygon bounded by multiple curves.
               After each SEGMENT MINUS (or SEGMENT PLUS), the area up
               to that point is displayed.


































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 103

                                 SIMPLE CURVE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          69  SI C         DESC  BT  PC PI PT  DCA  CA  SGN


         Computes additional (see below) data on a circular curve,
         given the following information:

         DESC = Curve identification number (1-999)
         BT   = Known point number on Back Tangent.
         PC   = Known Point of Curvature number.
         PI   = Known Point of Intersection of tangents number.
         PT   = Known Point of Tangency number.
         DCA  = Degree of Curve (Arc Definition) in Deg Min Sec.
         CA   = Central Angle of curve in Deg Min Sec.
         SGN  = +1.0 for clockwise curve, -1.0 for counterclockwise,

         OUTPUT: Curve number, coordinates of PC, PI, and PT, tangent
                 length from PC to PI, length of arc, foreward azimuth
                 from PI to PT, and back azimuth from PC to PI.

         NOTE: This command must be used independently of any other
               commands.  The commands COORD POA, COORD OFFSET, STA
               FROM COORD, and OFFSET ALIGNMENT cannot be used on a
               curve entered by SIMPLE CURVE.






























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 104

                                 SIMPLE SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          70  SM S         DESC  BT  TS  PI  SC  X  DCA  SIGN


         Given the above input variables, this command computes the
         other parameters associated with a simple spiral.  The
         equations used are defined in "Route Surveying & Design" by
         Thomas Hickerson published by McGraw-Hill.

         NOTE: A "spiral in" is the transition from a straight line to
               a curve as you are entering the figure.
               A "spiral out" is the transition from a curve to a
               straight line as you are exiting the figure.

         DESC = The number of the curve (1-999)
         BT   = Known point on Back Tangent of "spiral in" line
         TS   = Known point of Tangent to Spiral Transition "spiral
                in", or number assigned for "spiral out"
         PI   = Number assigned to Intersection of spiral tangents
         SC   = Number assigned to Spiral to Curve transition of
                "spiral in", or known point of Spiral to Curve
                transition of "spiral out"
         X    = Known length of spiral curve from TS to SC as "spiral
                in" (-X for spiral out)
         DCA  = Degree of Curve of circular curve
         SIGN = +1.0 for spiral clockwise, -1.0 for counterclockwise

         OUTPUT: Curve number DESC, SIGN, spiral length, degree of
                 curvature of circular curve, deflection angle at
                 spiral PI, long tangent length and azimuth, and the
                 coordinates of TS, SC, and PI.























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 105

                                 SPIRAL LENGTH


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          71  S L          DESC  TS  SC  PI  TSA  SIGN


         Given the above input variables, this command computes the
         entering spiral length (spiral in) only.  The equations used
         are defined in "Route Surveying & Design" by Thomas Hickerson
         published by McGraw-Hill.

         NOTE: A "spiral in" is the transition from a straight line to
               a curve as you are entering the figure.
               A "spiral out" is the transition from a curve to a
               straight line as you are exiting the figure.

         DESC = The number of the curve (1-999)
         BT   = Known point on Back Tangent of "spiral in" line
         TS   = Known point of Tangent to Spiral
         PI   = Number assigned to Point of Intersection of tangents
         SC   = Known point of Spiral to Curve
         TSA  = Azimuth of "spiral in" entering tangent at TS
         SIGN = +1.0 for spiral clockwise, -1.0 for counterclockwise

         OUTPUT: Curve number DESC, spiral length from TS to SC,
                 degree of curvature at SC, the tangent lengths and
                 their azimuths, and the coordinates of TS, PI, and
                 SC.




























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 106

                                 SPIRAL OFFSET


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          72  S O          POS OFFJ


         Find a point POS on a spiral that has been previously defined
         by the commands SIMPLE SPIRAL or SPIRAL LENGTH, corresponding
         to an offset J from the spiral.

         OUTPUT: Coordinates of POS, arc length along spiral from the
                 "tangent to spiral" transition point to POS, and the
                 offset distance from OFFJ to POS.











































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 107

                                 SPIRAL SPIRAL


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          73  SPR SPR      I  TS2  BTA2  X2  R2


         Computes the intersection I of a previously defined spiral
         (Spiral 1) with a second spiral (Spiral 2).  Spiral 1 must
         have been previously defined by a SIMPLE SPIRAL or SPIRAL
         LENGTH command.

         I    = Number assigned to the intersection of the spirals
         TS2  = Known Point of Tangency of Spiral 2
         BTA2 = Back Tangent Azimuth of Spiral 2 (PT to PI)
         X2   = Length of Spiral 2
         R2   = Radius of circular curve of Spiral 2; +R2 for
                clockwise, -R2 for counterclockwise

         OUTPUT: Point of intersection I and its coordinates, distance
                 from TS1 to the I, and distance from TS2 to I.




































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 108

                                 START OF JOB


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          74  S O J        FILENO


         This command resets all indicators, heads the 1st page with
         the file label, and is used to begin a new job.

         The FILENO can be any integer between 1 and 999.  When a new,
         unused file number is specified and coordinates are assigned
         to it, that file number becomes the filename and is saved to
         disk when END OF JOB or END OF RUN commands are invoked.

         If an existing file number is specified, then the point
         numbers, coordinates, figures, and plot files of that
         file number will be read into memory and used.  This will
         allow you to add to, change, or otherwise alter any existing
         file.

         If no file number is specified (just S O J - then [RETURN]),
         the program will function properly except that when you
         perform an END OF JOB or END OF RUN command to exit, the file
         that resides in memory WILL NOT BE SAVED TO DISK; it is
         considered a temporary file which WILL BE LOST!!!


          ----------------------------------------------------------
         |                                                          |
         |         DO NOT BEGIN A JOB WITHOUT A FILE NUMBER         |
         |                                                          |
         |       UNLESS YOU INTEND TO CREATE A TEMPORARY FILE.      |
         |                                                          |
         |                                                          |
         |            T H E   T E M P O R A R Y   F I L E           |
         |                                                          |
         |                W I L L   B E   L O S T !!!               |
         |                                                          |
          ----------------------------------------------------------

















          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 109

                              STATION AND OFFSET


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          75  S A O        DESCA  J  STAJ  DESCB


         This command computes the stations and offset distances to
         the known alignment DESCA whose stationing is defined by
         known point J having a known station value of STAJ.  DESCB
         is the description (or figure #) of points to be located by
         station and distance from DESCA.


         EXAMPLES: S A O (1 2) 1 1000 (5)   Print the sta. and offset
                                            to the alignment from
                                            point 1 to 2 (sta. of
                                            point 1 is 10+00) of point
                                            5.
                 : S F 465 (70-75 C3R-9)
                   S F   8 (200-256)
                   S A O 465 32 1423.6 8    Print the sta. and offsets
                                            to the alignment described
                                            in figure 465, whose
                                            stationing is defined by
                                            point 32 having station
                                            14+23.6, of each point in
                                            figure 8.

                 : S A O 465 32 1423.6 (490-2)
                                            Print the sta. and offsets
                                            to the same alignment as
                                            above, except print to
                                            points 490 and 2.























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 110

                           STATION FROM COORDINATE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          76  S F C        POA


         Compute the station of known point on arc POA.

         The curve must have been previously defined by a DEFINE CURVE
         or ALIGNMENT command.














































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 111

                                     STORE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          77  STR          J  Y  X


         Store as point number J the +North/-South coordinate Y and
         the +East/-West coordinate X.


         In all coordinate value assignments, the standard algebraic
         sign conventions apply:

              North and East coordinates are signed positive.
              South and West coordinates are signed negative.









































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 112

                                 STORE FIGURE


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          78  STO FIG      J  DESC


         Store all point numbers or other figures specified in DESC in
         the figure number J.  J should be in the range 1 to 9999.

         As an insight to figure storage, note that the point numbers
         (but not their coordinates) are stored as the figure file.

         The coordinates specified in DESC can be typed in as 1
         continuous string without pressing [ENTER] until all have
         been input.

         If the figure J has been previously defined, the new DESC
         will replace the old one.  Note that a figure may be a base
         line, an opened or closed property line or polygon, or any
         group of points.

         To reduce disk access times, try to keep the range of
         coordinate numbers as narrow as possible.

         EXAMPLE: The following 2 commands accomplish the same thing.

         STO FIG 8 (34 18 3 4 5 6 8 9 10 11 12 25 39 38 37 36 35 34)
                                      or
                      STO FIG 8 (34 18 3-6 8-12 25 39-34)

         If another figure number is entered as the DESC, then figure
         J will be stored as a duplicate of the figure entered as
         DESC.
                                STO FIG 60 8

         Figure 60 is now identical to figure 8.

         Also note that a figure may be described as containing one or
         more curves.  This is done by listing the point number of the
         PT, a space, the letter "C", the vertex point number, the
         letter R or letter L (for curve right or left), a space, and
         the point number of the PC.  For example:

                    STO FIG 345 ( 1-10 11 C12R 13 65-101 )

                         Where: 11 = PC
                                 C = Curve Identifier
                                12 = Vertex
                                 R = Arc To The Right
                                13 = PT

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 113

                                   STORE JOB


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          79  STO JOB      FILENO


         Store the project currently being computed to the default
         data disk as file FILENO, where FILENO is any number from
         1 to 999.

         This command is used primarily when a job is initially begun
         without assigning a file number after the START OF JOB
         command.  As described in the instructions for START OF JOB,
         a temporary file can be established when beginning a new
         project by invoking the START OF JOB command then immediately
         pressing [ENTER] without appending a file number.  When you
         are finished, invoking END OF JOB or END OF RUN will not save
         your project to disk, and all points, coordinate values, and
         figures will be lost.

         However, if you invoke STORE JOB ### (where 1<###<999) before
         exiting via END OF JOB or END OF RUN, then the file will be
         saved to your disk as file CG###.  You must then exit the job
         or program normally via END OF JOB or END OF RUN.  For all
         future access of that file, it is treated as if it were
         created normally via START OF JOB ###.






























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 114

                               STREETS INTERSECT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          80  S I          R DESCA WA DESCB WB M I VLL VLR VRL VRR

         Locate the intersection of two streets, including the PC's,
         vertices, and PT's of street corners whose radius is +R (or
         PI's only if R=0).

         R     = Known value of radius of street corner.
         DESCA = Known centerline description of street A figure
         WA    = Known width of street A
         DESCB = Known centerline description of street B figure
         WB    = Known width of street B
         M     = Known point - locate I nearest +M or farthest -M
         I     = Assigned Point of Intersection of the centerlines

         VLL   = Vertex of street corner, or PI of intersection if
                 R=0, at the left side of both streets.
         VLL+1 = PC, on street A, of corresponding corner (if any).
         VLL+2 = PT, on street B, of corresponding corner (if any).

         VLR   = Vertex of street corner, or PI of intersection if
                 R=0, at the left of street A and right of street B.
         VLR+1 = PC, on street A, of corresponding corner (if any).
         VLR+2 = PT, on street B, of corresponding corner (if any).

         VRL   = Vertex of street corner, or PI of intersection if
                 R=0, at the right of street A and left of street B.
         VRL+1 = PC, on street A, of corresponding corner (if any).
         VRL+2 = PT, on street B, of corresponding corner (if any).

         VRR   = Vertex of street corner, or PI of intersection if
                 R=0, at the right side of both streets.
         VRR+1 = PC, on street A, of corresponding corner (if any).
         VRR+2 = PT, on street B, of corresponding corner (if any).

         R can be entered as a zero (0) to indicate no street radius
         corners exist; only the PI's of the tangents will thus be
         computed.  DESCA &/or DESCB can be specified as edge of
         street by making WA and/or WB equal zero (0), respectively.
         VLL, VLR, VRL, and/or VRR may equal zero (0) to indicate no
         operation in corresponding sector.  PC's are to be considered
         on street A and PT's on street B.  The intersection I may
         also be assigned a value of zero (0) to indicate the
         intersection of the centerlines is not to be stored.

         This command can also be used for intersecting a right-of-way
         with a centerline.







          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 115

                                    TANGENT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          82  T            PTL VL RL  PTS VS RS  /  SIGN  CROSS


         Locate points PTL and PTS as the end points of a common
         tangent to 2 circles.

         PTL   = Assigned Point on Tangent of Larger circle
         VL    = Known Vertex of Larger circle
         RL    = Known Radius of Larger circle
         PTS   = Assigned Point on Tangent of Smaller circle
         VS    = Known Vertex of Smaller circle
         RS    = Known Radius of Smaller circle
         CROSS = +1.0 for external tangents, -1.0 for internal
                 (cross) tangents; larger circle entered first.
         SIGN  = Select for one of two possibilities of either case.
                 A +1.0 indicates a clockwise angle observed at the
                 intersection of a straight line projected from VL to
                 VS with a straight line projected from PTL to PTS;
                 sighting VL, turning to PTL.
                 A -1.0 indicates a counterclockwise angle observed at
                 the intersection of a straight line projected from VL
                 to VS with a straight line projected from PTL to PTS;
                 sighting VL, turning to PTL.

         OUTPUT: Coordinates of PTL and PTS, distance and azimuth of
                 the tangent from PTL to PTS.



























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 116

                                TANGENT OFFSET


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          83  T O          I  OP  BEGIN  END


         Compute the intersection I of a perpendicular offset point OP
         to a point on a line defined by connecting points BEGIN and
         END.


         EXAMPLE:
                                       OP
                                       |
                                       |
                                       |
                                       | 90deg
                    ----BEGIN--------- I -----------END----


         OUTPUT: Coordinates of I, distances from BEGIN to I and I to
                 OP.


































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 117

                                TRAVERSE ANGLES


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          84  T AN         DESC


         Traverse the points in figure or description DESC and print
         the coordinates, angles, and distances.

         This command is similar to AREA AZIMUTHS or AREA BEARINGS
         except that no area is printed and the 1st point may be
         different from the last.

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 118

                               TRAVERSE AZIMUTHS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          85  T AZ         DESC


         Traverse the points in figure or description DESC and print
         the coordinates, azimuths, and distances.

         This command is similar to AREA AZIMUTHS or AREA BEARINGS
         except that no area is printed and the 1st point may be
         different from the last.

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 119

                               TRAVERSE BEARINGS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          86  T B          DESC


         Traverse the points in figure or description DESC and print
         the coordinates, bearings, and distances.

         This command is similar to AREA AZIMUTHS or AREA BEARINGS
         except that no area is printed and the 1st point may be
         different from the last.

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 120

                             TRAVERSE DEFLECTIONS


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          87  T D          DESC


         Traverse the points in figure or description DESC and print
         the coordinates, deflections, and distances.

         This command is similar to AREA AZIMUTHS or AREA BEARINGS
         except that no area is printed and the 1st point may be
         different from the last.

         DESC may take the form of a figure number, or, a series of
         coordinate point numbers - (#xxx #xxx #xxx.....#xxx).  It is
         suggested that wherever possible, put the points in a figure.








































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 121

                                  TYPE PRINT


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          88  T P          N


         This command allows flexibility in producing output on your
         lineprinter.

         If N =  0, no input/output is echoed to the printer or
                    screen.
         If N =  1, only output data is echoed to printer (but not
                    screen).
         If N = -1, only error messages will output to printer (but
                    not screen).

         All line and page numbering that would ordinarily update
         during printer output is suspended while TYPE SCREEN is in
         effect.  When TYPE PRINT is re-invoked, line and page
         numbering takes place from where it was suspended by the last
         TYPE SCREEN command.  If you alternately call the TYPE SCREEN
         and TYPE PRINT commands during the course of a single
         session, we suggest that you follow each TYPE PRINT command
         with two asterisks (**), as illustrated below:

         >>TYPE PRINT [RETURN]
         >>**         [RETURN]

         This will execute a "top-of-form" command to your printer so
         that you can begin the current phase of your session at the
         top of a fresh page.

























          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 122

                                  TYPE SCREEN


         CODE ABBREVIATION INPUT VARIABLES
         ~~~~ ~~~~~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
          89  T S          N


         This command allows flexibility in producing output on your
         lineprinter.

         If N =  0, no input/output is echoed to the printer or
                    screen.
         If N =  1, only output data is echoed to screen (but not
                    printer).
         If N = -1, only error messages will output to screen (but
                    not printer).


         All line and page numbering that would ordinarily update
         during printer output is suspended while TYPE SCREEN is in
         effect.




































          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 123

                               OPERATING ERRORS


           ERROR MESSAGE   COMMAND#              CAUSE
         ~~~~~~~~~~~~~~~~~ ~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         Arc Is Greater       23    The distance along the spiral as
         Than Spiral                specified in input is greater than
         Length                     spiral length as currently stored.

         Area Not Found        1    No position can be found for the
         After 20 Tries             sides being adjusted which gives
                                    the desired area.

         Invalid Input      (many)  The data is not in accordance with
                                    input specifications for that
                                    particular command.

         Distance Is 0      51, 52  The distance was entered as zero;
                            53, 54  only real numbers other than 0 are
                                56  to be entered.

         Figure X Changed     44    You're warned that you're changing
                              78    a figure; it is printed in case
                                    you wish to restore it.

         First Point         1,  9  You have inadvertently asked for
         Different From     10, 11  the area of an open traverse.
         Last                       Hey, we've all done it at one time
                                    or another!

         Invalid Command    (none)  Column 1 contains a character
                                    other than an asterisk or blank
                                    indicating it is the 1st letter of
                                    a command, but the command can't
                                    be recognized.

         Invalid Figure X   (many)  The figure number specifed is not
                                    in the range 1 to 9999.

         Invalid Number       32    The number of parts specified is
         Of Parts X           33    not positive.
                              34

         Invalid Point X    (many)  You have attempted to store a
                                    point whose number is less than or
                                    equal to 0..or..greater than the
                                    combined lengths of the coordinate
                                    area and unused area..or..greater
                                    than 9999.

         Invalid Point        32    The points to be defined as
         Range X to Y         33    specified by the starting point
                              34    number and number of parts,
                                    includes at least 1 invalid point.




          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 124

                               OPERATING ERRORS


           ERROR MESSAGE   COMMAND#              CAUSE
         ~~~~~~~~~~~~~~~~~ ~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         Invalid Station      64    The station interval specified is
         Interval X                 not positive.

         Job X Terminated     74    A START OF JOB has been invoked
                                    during a job..or..a current job is
                                    being terminated so a new one can
                                    start.

         Larger Radius        82    The 1st radius entered is smaller
         Must Be First              than the 2nd and SIGN and CROSS
                                    have been specified.

         No Angle             32    One of the sides of the angle to
                                    be divided has a length of zero
                                    and therefore no direction.

         No Curve Defined   21, 22  A curve must be previously stored
                            57, 76  by an ALGNMENT or DEFINE CURVE
                                    command; this was not done.

         No Intersection    (all    The specified elements do not
                         intersect  intersect..or..the intersection
                         commands)  cannot be computed because of some
                                    condition noted earlier.

         No Line              60    The points specified to define the
                                    line have the same coordinates and
                                    thus do not define a unique line.

         No Offset            72    No offset can be computed because
         Possible             83    of a prevously noted error
                                    condition..or..in the case of
                                    tangent offset the two points
                                    defining the line are the same
                                    ..or..in the case of spiral offset
                                    the offset does not fall on the
                                    spiral or has not been computed
                                    after 1000 tries.

         No Previous           2    The station has been specified as
         Curve To Define            -1, meaning the stationing is to
         Stationing                 carried foreward from the prior
                                    curve, but no prior curve has
                                    been stored by an ALIGNMENT or
                                    DEFINE CURVE command.

         No Spiral          23, 25  These commands require a spiral to
         Defined            47, 72  be stored by SIMPLE SPIRAL, SPIRAL
                                73  LENGTH, or COMPOUND SPIRAL command
                                    which was not done.



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 125

                               OPERATING ERRORS


           ERROR MESSAGE   COMMAND#              CAUSE
         ~~~~~~~~~~~~~~~~~ ~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         No Tangent            83   No tangent is computed because of
         Possible                   a prior noted error condition
                                    ..or..because one circle lies
                                    entirely within the other..or..
                                    a cross tangent between
                                    intersecting circles has been
                                    requested.

         Point X            (many)  New coordinate values are
         Changed                    replacing prior ones.

         Point X or Y Out       1   Points X and Y were specified as
         Of Sequence                the start and end points of the
                                    sides to be adjusted; however, one
                                    of these points is not in the
                                    description..or..one of them is
                                    the 1st or last point in the
                                    description..or..Y preceeds X in
                                    the description.

         Radius Less           66   The distance between the 2 points
         Than 1/2 Chord        67   specified is less than 1/2 the
                               68   chord; they therefore cannot be on
                                    the curve.

         Second Figure         20   The description of the points to
         Smaller Than 1st           be defined contains fewer points
                                    than the number of points to be
                                    converted.

         Side At X Has          1   The adjustment required is so
         Changed Direction          great that the sides of the
                                    figure no longer intersect unless
                                    they extend backwards.

         Tangent Length        42   The two points specified to define
         Is Zero                    one of the tangents are identical
                                    and do not define a line.

         These Figures         43   The description specifying points/
         Have Different        44   figures to be defined and the
         Lengths                    description specifying points/
                                    figures used to define them show
                                    dissimiliar quantities.

         Undefined           1, 51  Two points which define a line
         Direction          54, 56  are identical.

         Undefined          (many)  You have requested use of a
         Figure X                   presently undefined figure.



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 126

                               OPERATING ERRORS


           ERROR MESSAGE   COMMAND#              CAUSE
         ~~~~~~~~~~~~~~~~~ ~~~~~~~~ ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
         Undefined          (many)  You have requested use of a
         Point X                    presently undefined point.

         Undefined             42   The radius was not specified
         Radius                     in the input not is it defined
                                    by coincidence of BT and PC
                                    or PT and FT.


         *************************************************************
         * WHENEVER AN ERROR IS DETECTED, 4  QUICK BEEPS WILL SOUND. *
         * DURING THE CONDUCT OF A COGO SESSION, THIS WILL SEEM LIKE *
         * A HECK OF A RACKET.  HOWEVER, TO CONTINUE BANGING AWAY AT *
         * THE KEYBOARD NOT AWARE THAT AN ERROR HAS OCCURED COULD BE *
         * CATASTROPHIC.  PAY ATTENTION TO THE SCREEN DURING BEEPS!! *
         *************************************************************



         Every effort has been made to install "error traps" at those
         points in the program where we anticipate the majority of
         errors might occur.  There might be arithmetic errors, or
         logic errors, or operator input errors.  Whatever the type,
         we have attempted to foresee their occasion.  The "traps" are
         designed to provide warning that a catastrophic error (one
         that will exit COGO to DOS, with loss of all data) could
         occur.  They should inform of this potential then offer the
         user an alternative.  Other "traps" simply announce what may
         or may not be errors.  These are most often cases where the
         user has induced a change in data value, such as assigning
         new coordinate values to an occupied point number.  Different
         "traps" yet will announce that the input variables to a
         command were incomplete.

         Error traps can be only so effective in helping to protect a
         user from himself before the warnings actually become a
         liability due to their numbers and audible/optical assaults
         on an operator's senses.  When overloaded with these beeps at
         every action, you may wish to turn them off - negating their
         usefulness, or simply find that this isn't the COGO for you.
         Hopefully, we have achieved an efficient compromise.

         If you find that you are being incessantly beeped at or,
         instead, are not being properly warned of hazards, please
         report your difficulties to us via the report forms at the
         end of this manual.







          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 127

                               A SAMPLE SESSION
                               INTERACTIVE MODE


         The following sample project is intended only to demonstrate
         to you the basic commands and allow you to interact with COGO
         while running a sample job whose outcome is known.  However,
         please note that this is not meant to be a detailed
         instructional text on the techniques of using COGO, but
         rather a fast introduction to the mechanics of using the
         commands and data entry in an INTERACTIVE MODE.  Before using
         COGO for your own projects, please do run this sample job to
         get familiar with COGO.

         Although the sample problem describes a very basic geometric
         figure, it should assist novice users in understanding what
         COGO is all about: THE ASSIGNMENT OF COORDINATES TO ANY POINT
         WILL COMPLETELY IDENTIFY AND LOCATE THAT POINT FOR ADDITIONAL
         USES.  The commands STORE, LOCATE BEARING, LOCATE ANGLE,
         BEARING INTERSECT, INVERSE BEARING, and AREA BEARINGS are
         used and explained as the solution progresses.

         There are two distinct modes in which data can be entered
         into the COGO program: INTERACTIVE...real-time via the
         keyboard (in much the same fashion as you "punch out" a
         solution on your hand calculator), and BATCH...where all the
         commands and data are assembled and fed into COGO at one
         time.  First, we will run in INTERACTIVE mode.

         We will assume that you have powered up COGO and are now at
         the COGO prompt >>.  From this point on, all of the commands
         and data that you would type are preceeded by the COGO prompt
         >>.  All COGO output and responses follow your input.


         ************************************************************
         *         -----------------------------------------        *
         *        | Start the job and give it a file number |       *
         *        |         The file number is 234.         |       *
         *         -----------------------------------------        *
         *                                                          *
         *>>S O J 234                                               *
         *                                                          *
         ***********************************************************


         ************************************************************
         *       ---------------------------------------------      *
         *      | Store the POB coordinates in point number 1 |     *
         *       ---------------------------------------------      *
         *                                                          *
         *>>STORE 1 10000 10000                                     *
         *                                                          *
         *    STORE     1                                           *
         *                                                          *
         ************************************************************


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 128

                               A SAMPLE SESSION
                               INTERACTIVE MODE

         ************************************************************
         *          --------------------------------------          *
         *         | Traverse the first course, #1 to #2  |         *
         *          --------------------------------------          *
         *                                                          *
         *>>LOCATE BEARING 1 2 N 23 25 26 E 326.247                 *
         *                                                          *
         *              2         10299.3606          10129.6931    *
         *                                                          *
         ************************************************************



         ************************************************************
         *      ----------------------------------------------      *
         *     | Traverse the 2nd course to the PC of a curve |     *
         *     |               The PC is point 3.             |     *
         *     |  Note "repeatability" & blank in 1st column. |     *
         *      ----------------------------------------------      *
         *                                                          *
         *>> 2 3 N 23 25 26 E 121.163                               *
         *                                                          *
         *              3         10410.5385          10177.8591    *
         *                                                          *
         ************************************************************



         ************************************************************
         *   ----------------------------------------------------   *
         *  | Traverse the 3rd course to the vertex of the curve |  *
         *  |                The vertex is point 4.              |  *
         *   ----------------------------------------------------   *
         *                                                          *
         *>>LOCATE ANGLE 2 3 4 -90. 110.                            *
         *                                                          *
         *              4         10366.8101          10278.7939    *
         *                                                          *
         ************************************************************



         ************************************************************
         *     ------------------------------------------------     *
         *    | Traverse the 4th course to the PT of the curve |    *
         *    |                The PT is point 5.              |    *
         *    |   Note "repeatability" & blank in 1st column.  |    *
         *     ------------------------------------------------     *
         *                                                          *
         *>> 3 4 5 90. 110.                                         *
         *                                                          *
         *              5         10467.7449          10322.5223    *
         *                                                          *
         ************************************************************

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 129

                               A SAMPLE SESSION
                               INTERACTIVE MODE

         ************************************************************
         *       --------------------------------------------       *
         *      |     Traverse the 5th course to point 6.    |      *
         *      | Note "repeatability" & blank in 1st column |      *
         *       --------------------------------------------       *
         *                                                          *
         *>> 4 5 6 -90. 110.                                        *
         *                                                          *
         *              6         10424.0166          10423.4570    *
         *                                                          *
         ************************************************************




         =============================================================
         | From this point on, all commands will be entered as codes |
         |   and all directions will be entered as quadrant codes.   |
         |    This is considered the "expert" mode of data entry.    |
         =============================================================



         ************************************************************
         *           ------------------------------------           *
         *          | Traverse the 6th course to point 7 |          *
         *           ------------------------------------           *
         *                                                          *
         *>>53 6 7 3 24 13 42 562.875                               *
         *                                                          *
         *              7          9910.7211          10192.4678    *
         *                                                          *
         ************************************************************



         ************************************************************
         *           -------------------------------------          *
         *          | Inverse between the POB point 1 and |         *
         *          |     the last calculated point 7.    |         *
         *           -------------------------------------          *
         *                                                          *
         *>>46 1 7                                                  *
         *                                                          *
         *    FROM   1  TO   7       S 65 06 54.378 E     212.1664  *
         *                                                          *
         ************************************************************








          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 130

                               A SAMPLE SESSION
                               INTERACTIVE MODE

         *************************************************************
         *  -------------------------------------------------------  *
         * |   Assign point 8 by intersecting line 6 to 7 with a   | *
         * |         perpendicular radiating from point 2.         | *
         * |             This is the subdivision line.             | *
         *  -------------------------------------------------------  *
         * |    Note that we have used the angle delimiters to     | *
         * | specify the bearings - see pages 28 - 30 for examples | *
         *  -------------------------------------------------------  *
         *                                                           *
         *>>18 8 2 (A 1 2 - 90.) 6 (A 6 7)                           *
         *                                                           *
         *              8 INTERSECTION ANGLE = 89 11 44.000          *
         *              8      10213.1942       10328.5844           *
         *                                                           *
         *************************************************************




          ==========================================================
         | Our project is now divided into 2 lots - north and south |
         |                Store both lots as figures.               |
          ==========================================================




         ************************************************************
         *              ------------------------------              *
         *             | Store north lot as figure #1 |             *
         *              ------------------------------              *
         *                                                          *
         *>>78 1 (2 3 C4R 5 6 8 2)                                  *
         *                                                          *
         *    STORE FIGURE 1                                        *
         *                                                          *
         ************************************************************



         ************************************************************
         *              ------------------------------              *
         *             | Store south lot as figure #2 |             *
         *              ------------------------------              *
         *                                                          *
         *>> 2 (1 2 8 7 1)                                          *
         *                                                          *
         *    STORE FIGURE 2                                        *
         *                                                          *
         ************************************************************




          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 131

                               A SAMPLE SESSION
                               INTERACTIVE MODE


         ************************************************************
         *      ----------------------------------------------      *
         *     | Compute the area and display course bearings |     *
         *     |          and distances of north lot.         |     *
         *      ----------------------------------------------      *
         *                                                          *
         *>>11 1                                                    *
         *                                                          *
         *    AREA BEARINGS                                         *
         *       1                                                  *
         *              2  10299.3606  10129.6931                   *
         *                             N 23 25 26.000 E  121.1630   *
         *              3  10410.5385  10177.8591                   *
         *                             S 66 34 34.000 E  110.0000   *
         * CC 4 10366.8101 10278.7939 DELTA=90 00 00.000R L=172.7876*
         *                             N 23 25 26.000 E  110.0000   *
         *              5  10467.7449  10322.5223                   *
         *                             S 66 34 34.000 E  110.0000   *
         *              6  10424.0166  10423.4570                   *
         *                             S 24 13 42.000 W  231.1858   *
         *              8  10213.1942  10328.5844                   *
         *                             N 66 34 34.000 W  216.7542   *
         *              2  10299.3606  10129.6931                   *
         *                                                          *
         *    AREA =     47884.025 SQ.FT. =     1.09926595 ACRES    *
         *                                                          *
         ************************************************************



         ************************************************************
         *      ----------------------------------------------      *
         *     | Compute the area and display course bearings |     *
         *     |          and distances of south lot.         |     *
         *      ----------------------------------------------      *
         *                                                          *
         *>> 2                                                      *
         *                                                          *
         *    AREA BEARINGS                                         *
         *       2                                                  *
         *              1  10000.0000  10000.0000                   *
         *                             N 23 25 26.000 E  326.2470   *
         *              2  10299.3606  10129.6931                   *
         *                             S 66 34 34.000 E  216.7542   *
         *              8  10213.1942  10328.5844                   *
         *                             S 24 13 42.000 W  331.6892   *
         *              7   9910.7211  10192.4678                   *
         *                             N 65 06 54.378 W  212.1664   *
         *              1  10000.0000  10000.0000                   *
         *                                                          *
         *    AREA =     70542.041 SQ.FT. =     1.61942242 ACRES    *
         *                                                          *
         ************************************************************

          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 132

                               A SAMPLE SESSION
                                  BATCH MODE

         If you entered the commands and data of the sample problem in
         interactive mode, you might now have developed a slightly
         grudging respect for the power and versatility of COGO,
         despite having used only the most basic of its commands.  As
         you become more comfortable with COGO and versed in its
         command structure, you will develop an awareness of its
         tremendous capabilities.  To become thoroughly skilled in its
         use, all we can suggest is practice, practice, practice.  The
         more you use it, and the more diverse the commands you use,
         the more efficient you will become.

         Finally, to demonstrate the BATCH MODE of using COGO, we have
         placed the entire list of commands and data that created
         figures 1 and 2 on your data disk in 2 ASCII files.  They are
         files CG234PRO.INP and CG234COM.INP, were created in our word
         processor, and are listed below as they appear on disk (from
         your DOS A> prompt, type TYPE B:CG234PRO.INP or TYPE
         B:CG234COM.INP to view them on your screen).  Instead of
         being run interactively from the keyboard as we did in the
         preceding pages, the subdivision project could have been
         typed into a file, using your word processor or text editor.
         The job could then have been run at any time via the BATCH
         command, which places COGO into the BATCH mode of operation
         (as opposed to INTERACTIVE mode).

         THE BATCH MODE RECOGNIZES, ACCEPTS, AND EXECUTES COMMANDS AND
         INPUT DATA CONTAINED IN AN ASCII TEXT FILE, JUST AS IF THOSE
            SAME COMMANDS AND INPUT DATA WERE BEING ENTERED BY THE
                   OPERATOR VIA THE KEYBOARD, INTERACTIVELY.

         The primary advantage to BATCH mode is that if there was a
         mistake in any of the data, you do not have to manually
         re-enter the entire job, after correcting the error, from the
         keyboard as you would have had to do in interactive mode.
         You could instead correct just the erroneous data in your
         editor/word processor then re-run the BATCH.  The peripheral
         advantages to running projects in the BATCH mode are many,
         but it primarily allows a documented, orderly listing of all
         input/output (via the printer) for a complex project,
         provides for convenient error correction, and allows
         execution by non-technical personnel.

         If you use the command BATCH SCREEN on either CG234PRO or
         CG234COM, then the complete solution will scroll across your
         monitor as it occurs.  If you use the command BATCH PRINT,
         then no display will occur on your monitor but will instead
         output to the printer, providing you with a printed record of
         the commands, input data, and output resultants.  Note that
         this will allow evaluation and analysis of the complete
         solution process as it took place!  Please note that
         coordinates created via the BATCH mode are no different than
         if they had been created in INTERACTIVE mode; they must be
         saved to disk via the END OF JOB or END OF RUN commands too.


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 133

                               A SAMPLE SESSION
                                  BATCH MODE

         First, run the CG234COM.INP file & output to screen only:

         1) From the COGO prompt >>, type  S O J 234    & [RETURN]
         2) From the COGO prompt >>, type  BATCH SCREEN & [RETURN]
         3) In response to query,    type  CG234COM     & [RETURN]

         Now, run the CG234PRO.INP file & output to printer only:

         1) From the COGO prompt >>, type  S O J 234    & [RETURN]
         2) From the COGO prompt >>, type  BATCH PRINT  & [RETURN]
         3) In response to query,    type  CG234PRO     & [RETURN]

         Note that before invoking the BATCH command, we started job
         #234 by using the START OF JOB command to activate the
         coordinate file; you can't run a job unless the file is 1st
         opened on the disk.  Note also that when the batch command
         prompted us to enter the batch file's name, we entered
         CG234COM & CG234PRO, but WITHOUT the extension .INP; never
         enter the extension, although it MUST ALWAYS be assigned with
         the extension .INP (thats how it automatically finds it on
         the default data disk and distinguishes it from the normal
         coordinate file CG###).  Also, the commands of CG234PRO.INP
         all begin in column #1; this is absolutely required of all
         BATCH files, unless you want to invoke the "repeatability"
         feature of COGO by leaving a blank space in column 1 to
         repeat the prior command as illustrated in file CG234COM.INP.

         A batch file must have been created in an editor or the
         non-document (ASCII) mode of your favorite word processor.
         This means that the document must be stored on the disk
         without imbedded control codes or characters.  Registered
         users will receive a version that has the ability to call up
         an editor/word processor without having to exit COGO for
         creating and editing BATCH files.  So that you might
         experience the same capabilities using this version (1.22),
         we suggest that before running COGO, you install the SIDEKICK
         RAM-resident utility package by Borland International which
         also contains a mini word processor (the NOTEPAD feature).



              **************************************************
              *                                                *
              *      WHEN YOU CREATE AN ASCII BATCH FILE,      *
              *        SAVE IT TO THE DEFAULT DATA DISK        *
              *          WITH THE EXTENSION OF [.INP]          *
              *                                                *
              *     THE DEFAULT DATA DISK WILL BE SEARCHED     *
              *       AUTOMATICALLY FOR THE [.INP] FILE        *
              *       WHEN THE BATCH COMMAND IS INVOKED.       *
              *                                                *
              **************************************************



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 134

                               A SAMPLE SESSION
                                  BATCH MODE

                              File "CG234PRO.INP"


         The following BATCH file is typed in "PROper" mode - all
         commands are spelled out, comments are used liberally,
         spacing is used to improve readability, bearing directions
         are used instead of quadrant numbers, and repeating commands
         are re-typed.  In other words, this file can be easily
         understood and edited by anyone familiar with the COGO
         commands.


         **   COGO project to create "North" and "South" figures.
         *
         *    Store the origin in point #1.
         *
         STORE 1 10000 10000
         *
         *    Create perimeter points.
         *
         *  COMMAND       BS AP FS  DIRECTION/ANGLE  DISTANCE
         *~~~~~~~~~~~~~~  ~~ ~~ ~~  ~~~~~~~~~~~~~~~  ~~~~~~~~
         LOCATE BEARING    1     2    N 23 25 26 E   326.247
         LOCATE BEARING    2     3    N 23 25 26 E   121.163
         LOCATE ANGLE      2  3  4     -90.          110
         LOCATE ANGLE      3  4  5      90.          110
         LOCATE ANGLE      4  5  6     -90.          110
         LOCATE BEARING    6     7    S 24 13 42 W   562.875
         *
         *    Inverse from point #1 to point #7.
         *
         INVERSE BEARING 1 7
         *
         *    Intersect line 6-7 with a perpendicular from point 2.
         *
         BEARING INTERSECT 8 2 (A 1 2 - 90.) 6 (A 6 7)
         *
         *    Store the "North" parcel in figure #1.
         *    Store the "South" parcel in figure #2.
         *
         STORE FIGURE 1 (2 3 C4R 5 6 8 2)
         STORE FIGURE 2 (1 2 8 7 1)
         *
         *    Inverse bearings/distances & compute area of figure #1.
         *    Inverse bearings/distances & compute area of figure #2.
         *
         AREA BEARINGS 1
         AREA BEARINGS 2
         *
         *    End Of Job of file #234.
         *
         END OF JOB



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 135

                               A SAMPLE SESSION
                                  BATCH MODE

                              File "CG234COM.INP"


         The following BATCH file is typed in "COMmon" (or
         abbreviated) mode - all commands are identified by their menu
         numbers, comments are not used, spacing is not used to
         improve readability, quadrant numbers are used instead of
         bearing directions, and repeating commands are automatically
         invoked by leaving a space in column #1.  In other words,
         this could be considered the "expert" mode of batching,
         compressed and efficient - but very cryptic and difficult to
         understand, evaluate, and edit.  It performs exactly the same
         operations as the BATCH file of the preceding page.


         77 1 10000 10000
         53 1 2 1 23 25 26 326.247
            2 3 1 23 25 26 121.163
         51 2 3 4 -90. 110
            3 4 5 90. 110
            4 5 6 -90. 110
         53 6 7 3 24 13 42 562.875
         46 1 7
         18 8 2 (A 1 2 - 90.) 6 (A 6 7)
         78 1(2 3 C4R 5 6 8 2)
            2(1 2 8 7 1)
         11 1
            2
         35



         NOTE: There are no appreciable execution speed differences
               between PROper and COMmon batch files; however, the
               COMmon form of the batch file does take less disk
               space.



         ************************************************************
         *                                                          *
         *                      IT IS SUGGESTED                     *
         *                           THAT                           *
         *       ALL BATCH FILES BE CREATED IN "PROPER" FORMAT      *
         *                           FOR                            *
         *    COMPUTATIONS THAT WILL BE EVALUATED AT A LATER DATE   *
         *                            OR                            *
         *      PROJECTS THAT MAY BE LATER AMMENDED OR CORRECTED    *
         *                                                          *
         ************************************************************





          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 136

                                  BUG REPORT


         NAME___________________________________   DATE_____________

         ADDRESS________________________________      DISK ENCLOSED?
                                                      Y____   N____
         CITY, STATE, ZIP_______________________
                                                    PRINTOUT ENCLOSED?
         TELEPHONE (     ) _______ _____________      Y____   N____


         Please describe, as precisely as possible, the nature of the
         error or bug:

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         If possible, please try to duplicate the error in a BATCH
         file.  If you can send the BATCH file to us (preferably on
         disk) it will speed up the correction process.

         All formal bug reporters will be given a 10% discount off the
         standard registration fees if they have not yet registered
         (however, we can not make this discount offer retroactive).

                        THANK YOU FOR YOUR COOPERATION!


          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 137

                            COMMENTS & SUGGESTIONS


         NAME___________________________________   DATE_____________

         ADDRESS________________________________      DISK ENCLOSED?
                                                      Y____   N____
         CITY, STATE, ZIP_______________________
                                                    PRINTOUT ENCLOSED?
         TELEPHONE (     ) _______ _____________      Y____   N____


         Please describe your comment or suggestion:

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         _____________________________________________________________

         If applicable, please try to illustrate your comments or
         suggestions in a BATCH file.  If you can send the BATCH file
         to us (preferably on disk) it will allow us to more easily
         evaluate your comments/suggestions.

         All formal comment/suggestion reporters will be given a 10%
         discount off the standard registration fees if they have not
         yet registered (however, we can not make this discount offer
         retroactive).

                        THANK YOU FOR YOUR COOPERATION!



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 138

                               ACKNOWLEDGEMENTS


         The creation of GeoCalc's COGO spanned several years, from
         its original conception as a micro based applications
         program, through its flow and algorithm design and coding, to
         its eventual assemblage and testing.  It occupied the time
         and services of many individuals and organizations during
         this process.  The following credits may at times get
         melancholy; we certainly don't want to bore or offend our
         users, but hey, these are our acknowledgements and we can get
         funky if we want.  When you write your acknowledgements, then
         you can do it your way.

         We would like to thank and recognize Jim Requa of
         TerraGraphics, Dr. Charles L. Miller of CLM/Systems, Inc.,
         and Ronald Leers of Charles H. Sells, Inc. for providing the
         original conceptions of COGO and historical documentation;
         Professor Steven Jochum of Temple University's College of
         Engineering & Architecture for establishing GeoCalc's COGO in
         his curriculum and helping us to "legitimize" the program;
         Bill, Don, and John Barton of Barton & Martin Consulting
         Engineers and Ed Bursich of Bursich & Associates for their
         willingness to help us test the code; Conrad L. Moore of C.
         L. Moore Land Surveying Inc. for extensive general testing;
         Israel Zeitz of the Philadelphia Bureau of Surveys & Design's
         4th Survey District for working on the spiral commands; all
         those individuals and their firms who have provided or
         offered material support, suggestions, and encouragement; and
         finally, Patricia and Carol Cleary and Patricia and Cynthia
         Havey for typing code and documentation until their
         fingernails got short, putting up with more late night/early
         morning antics and phone activity than a family of vampires,
         accepting virtual poverty or at least heavy debt because
         "...Honey, we REALLY need (take your choice) a compiler,
         another 1000 disks, to incorporate, another computer system
         for development, etc....", and generally supporting and
         assisting the project in the zillions of ways that test
         patience, endurance, and commitment.

         Thank you all.

















          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 139

                                FUTURE VERSIONS


         Our intent is to revise and improve COGO on a continuous
         basis.

         Of course, every attempt will be made to make these changes
         downwardly compatible with prior versions of COGO.  This is
         the reason for the spaces in the menu of this version (1.22).
         Re-alphabetizing the commands, and thus changing their menu
         numbers, would not allow batch files written on one version
         to run on a later version.  For example, suppose you create a
         batch file with this Ver. 1.22 in COMmon mode that uses the
         code number for LOCATE BEARING (#53).  When you register and
         receive an expanded version, if the code number of the LOCATE
         BEARING command has changed because of menu additions, that
         particular batch file will not run on the later version
         without an awkward or inconvenient conversion routine.

         Future versions of COGO will contain these functions (some
         of which are now being developed/tested):

         1.  Color
         2.  Screen plotting with unlimited zooming and real-time
                 panning via flip-up window (CGA, EGA, & PGA).
         3.  Vertical (elevation) coordinates: X, Y, and Z.
         4.  Some additional applications, such as
             a.  State Plane Coordinate/Latitude, Longitude
                 conversions.
             b.  Stadia.
             c.  Volumetric computations.
             d.  Cut/Fill computations with formal output sheet.
         5.  Conversion routines to address the popular CADD packages
                 and other COGO's so that data from these other
                 programs can be input to GeoCalc's COGO and
                 vice-versa.
         6.  A resident text editor to allow creation of batch files
                 without exiting COGO to a third party editor.
         7.  A toggle to activate automatic saving (in RAM) of
                 commands in interactive mode; this would allow error
                 correction similar to batch mode.
         8.  Compression/reduction of the program's code; its much too
                 large and we know it!  Many of the current routines
                 written in high level languages will be re-written in
                 low level languages.
         9.  Much better documentation.  The goal here is clear,
                 concise instructions without making the reference
                 manual a textbook.


         The above are some of many enhancements that are planned; the
         official "wish list" is quite long but can be changed at your
         requests via the suggestion form of page 137.  Note that some
         of the above will be resident within COGO while others are
         supplementary programs.



          GeoCalc COGO - Surveying/Engineering Applications Software





                                                              Page 140

                         CHRONOLOGY OF GEOCALC'S COGO


         VERSION  DESCRIPTION
         ~~~~~~~  ~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
           1.20   The original; released in limited quantities as a
                  beta test package in the Philadelphia area only.
           1.21   First national distribution.
           1.22   Current version...minor bugs of V 1.21 repaired.

















































          GeoCalc COGO - Surveying/Engineering Applications Software
LAYOUT 000
rBPB?Aú----\----+---------+---------+---------+---------+---------+---------+----/---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+----BPB?Aú\--------+---------+---------+---------+---------+---------+---------+---------/----+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+---------+----BP