# CGLine Wireless Monitoring Set

Pos.   )		Pcs.

CGLine Wireless Monitoring Set for a visualization on a mobile iPad Tablet PC of up to 400 pcs. CGLine self contained luminaires, split into 4 lines with up to 100 pcs. Luminaires each, in installations according to EN 50172, DIN VDE 010-718 and DIN V VDE V 0108-100.

All of the data and commands are transmitted via 2-core bus cables.

CGLine Wireless Monitoring Set contains a CGLine Web-Interface, WLAN-Access point with power supply in a wall mounting box and an iPad with Retina Display for a wireless visualization of the status of CGLine self-contained luminaires

Functions:

- CGLine Web-interface and WLAN Access-point in a wall mounting box for a wireless visualization of

up to 400 CGLine self-contained luminaires with an iPad tablet PC

- Integrated WEB-server for visualization via usually WEB-browser (e.g. Safari..)

- Any desired CGLine Wireless Monitoring sets with a tablet PC usable

- Status of all installed interfaces in the network visible, due to intelligent PING function.

- CGLine Web-Interface with block input with differential-loop monitoring (1 kOhm)

- Automatic luminaire search function (no manual addressing needed)

- Automatic function test, testing distance can be freely selected

- Automatic operating duration test, testing distance can be freely selected

- Split battery duration test: DT of even / uneven addresses are shifted for 24h

- Start / Cancel operating duration test manually

- Block the emergency lighting function (complete or by bus line)

- Luminaires in maintained mode a switchable OFF ( to non-maintained light, complete or each line)

- Display of the luminaire status (Switched ON/OFF)

- Constant charge monitoring

- Communication monitoring each luminaire / line / interface

- Recording the single fault messages

- Freely programmable potential-free alarm contact for battery operation, function test, operating

duration test, communication fault, luminaire fault or charging fault.

- LED displays: operation, test and fault

- Configurable password protection

- Removable configuration and test book memory via memory card for a period of at least 4 years

- Evaluation of the test book on memory card using optional card reader and CEAG software on a  
   standard PC

Technical data:

Wall mounting box:

Degree of protection: 			IP54

Housing:							Wall mounting box, plastic

Dimensions (mm): 				L=360mm, W=255mm, H=165mm

CGLine Web-Interface:

Supply voltage: 				230V AC

Power consumption:			< 4 Watt

Connection terminals: 		2.5 mm²

Ambient temperature:			0...50°C

CGLine connection:			4 x lines (2-core each) with up to 100 CGLine luminaires each

Alarm relay contact:			 1 x UM, 24 V 0.5A; freely programmable

Block input:						S1/S2 with differential loop monitoring, 1kOhm

LED displays: 		Power, sum failure, SD card, status, LAN connection (link),             CGLine (Tx/Rx)

WLAN-Access-Point:

Supply voltage: 				24V DC via internal power supply

Power consumption:			< 4,5 Watt

Transmission rate:				54 Mbit/s

Range:							max. 300m

DHCP-Server:					Automatic IP-assignment for up to 10 user

iPad tablet PC:

OS:								Apple iOS6

Processor:						Apple A6X Dual-Core

Memory:							32GB

Display:							9,7” IPS TFT-LED Backlight

Resolution:						2048 x 1536

Operation time:					up to 10 hours

Web browser:					Safari

Options:

... pcs. CGLine WiFi connection box for wall mounting with cable entries

... pcs. SD-card, formatted for CGLine PC-Interface

... pcs. Card-reader for SD memory card (for standard PC)

... pcs. CEAG PC Software CGLine 400 for configuration and test book evaluation (for windows based

standard PC)

Type:

Manufactured by: CEAG