本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.51wendang.com/doc/d18d862180e68ca57afad7bc

ACD2-MRL_SUR_EN1

[此处图片未下载成功]

-MRL System Start Up Routine

Otis Elevator Co., Ltd.

No.: ACD2-MRL_SUR_EN

-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 2/61

Start Up RoutinePack

Approval Prepared Su Xiaolei By Dep. DateAUTH. CAL7418 PDC 2010-03-16

By Dep. Date

Shan PDC 2010-03-23

By Dep. Date

Zubin PDC 2010-03-25

Version ComponentGECB GDCB SPBC_II/III

.W. VersionKBA26800ABG AXX26800AKT GAA26800NB1/GCA26800KX10

.W. VersionGAA30780DAG or higher AP230924CAE or higherGAA30760BAG/GAA30773BAE higher

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 3/61

Start Up RoutinePack

RecordItem 1 2 3 4 5 6 7 http://www.51wendang.com/doc/d18d862180e68ca57afad7bc8 9 10 11 12 13 14 15 16 17 18 19 20 Auth. PC CAL8052 Description of Change Add PARAMETERS SETUP AND TROUBLE SHOOTING 2010-8-28 (P32~61)Su Xiaolei

work and the information it contains are the property of Xizi Otis Elevator Company (“XOEC”). It is delivered to others on the express condition that it will be used only for, or on behalf of, XOEC; that neither it nor the information it contains will be reported or disclosed, in whole or part, without the prior written consent of XOEC, and that on demand it and any copies will be promptly returned to XOEC.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 4/61

Start Up RoutinePack

目录 1 REQUIREMENTS...........................................................................................http://www.51wendang.com/doc/d18d862180e68ca57afad7bc................................... 5 2 REFERENCES.................................................................................................................................... 5 3 Preliminary checks ............................................................................................................................. 6 4 Starting up in inspection .................................................................................................................. 114.1 4.2 4.3 4.4 Parameter Setup (GDCB): E/I- panel ....................................................................................................... 11 Encoder Adjustment= LRT (Locked Rotor Test) .................................................................................... 12 Check of Run -Direction ............................................................................................................................. 13 Manual Brake Release chehttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcck (E/I-panel) .................................................................................................. 14

Position Reference System Adjustment .......................................................................................... 15 6 Check of hoistway signals (PRS with RLEV/ADO).......................................

................................ 17 7 First Normal Running Preparation................................................................................................. 188.1 8.2 8.3 8.4 Start up of hoistway learn run ................................................................................................................... 19 Faults during Learn Run............................................................................................................................ 21 Find Bottom Landing Run ....................................................................................http://www.51wendang.com/doc/d18d862180e68ca57afad7bc..................................... 21 Viewing the Landing Table ......................................................................................................................... 22

DCS– Door Check Sequence (E/I-panel) ....................................................................................... 23 10 Normal operation .............................................................................................................................. 25 11 Balance Adjustment .......................................................................................................................... 25 12 Final Adjustment............................................................................................................................... 2612.1 Floor Level Adjustment .............................................................................................................................. 26 12.2 Start Jhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcerk, Rollback reduction ................................................................................................................... 27 12.3 Check of ADO and RLV (Option) .............................................................................................................. 28 12.4 Assignment for building configuration ..................................................................................................... 29 12.5 Position Indicator setup .............................................................................................................................. 29 12.6 Turnover test for code inspection............................................................................................................... 31

PARAMETERS SETUP AND TROUBLE SHOOTING .............................................................. 32

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下http://www.51wendang.com/doc/d18d862180e68ca57afad7bc载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 5/61

1

Start Up RoutinePack

Starting up of ACD2-MRL control system should be only performed by authorized person! Be sure the completion for cab and mechanical assemblies in hoistway, as well as correct connection for all electrical devices both in hoistway and controller before elevator works. Also some necessary check should be done before running.

——SVT User’s Guide - Manual(GAA30780DAG_STM)

——SVT User’s Gu

– Reference List (GAA30780DAG_REF)

(Inside Controller)

——Installation Parameter——I/O Lists

(GAA30780DAG_INS) (GAA30780DAG_IO)

——Operation Manual

(55661_AP230924CAE)

(Inside Hoistway)

——Component Start-Up&amp; Installation

(RBI_CSU_ZH)

Device(Inside Hoistway)://www.51wendang.com/doc/d18d862180e68ca57afad7bc

——AT120 Field Manual

(AT120_OIM_ZH) (DO2000_OIM_ZH) (AT400_OIM_ZH) (NGSOK_OIM_ZH)

(Top of car)

——DO2000 Field Manual——AT400 Field Manual——NGSOK Field Manual

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 6/61

33.1

Start Up RoutinePack

checksHint: before inspection run, all the mechanical components should be installed and adjusted. Confirm the elevator is in the ERO modePlug for INS Shunt: INS/NOR

for inspection run

.2

the controller and Emergency&amp; Inspection Panel Open the door of the controller and Emergency&amp; Inspection Panel, check whether the connection of the components is loosen or damaged or not, and keep the files of the elevator. Besides, change the parts which have damaged andhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc tighten all connections places on the control cupboard. Pay special attention to the power supply wires, motor wires and drive wires when you are tightening the connection.

.3

the wiring According to the wiring diagram, check the PVT cable, the temporal wirings in traveling cable and in limit switches, and check whether all the ground wires of equipments are in a reliable ground connection situation or not.

.4

the insulation The connection of ground wires and HL is shed out, then pulls out all plugs on the GECB, turn all breakers to the“OFF” position. Measure the insulation resistance value of the ground wires and HL, power supply wires, the motor brake wires, the door operator and both ends of the illumination with insulating apparatus. Ensures that the insulation resistance value meet the regulated value. ThenUnpublished Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]://www.51wendang.com/doc/d18d862180e68ca57afad7bcr

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 7/61

Start Up RoutinePack

ground wires and plug in all plugs back to GECB board again.

Dynamic circuit and safety circuit Control circuit (including door operator), illumination and signal circuit

Range≥0.5M ≥0.5M

: the connection plugs on the PCB board should be pulled out during the insulation test, or the PCB board may be damaged. 3.5 Check the input voltage Cut off the main power switch and other breaker in the controller, and check whether the input three-phase voltage is in the regulation range ( /-10%) or not. Adjust the wiring of the transformer terminals according to the real input voltage. Check the illumination voltage is for 220V /-10%. 3.6 Check the control transformer output voltage Turn on the main power switch, check whether the output vhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcoltage by the transformer match with the

( /-10%) or not. 3.7 Check the dynamic power wiring Before turn on the dynamic power wiring should be checked and be confirmed, the U/V/W/PE of TB2 should be connected to U/V/W/PE of motor one by one. Do not change the sequence of the three phases, or the elevator may run abnormally. 3.8 Check the remote serial link voltage Disconnect the controller connections 1C and 1H/1G. Check the Voltage of 1C4-1C3 (27-36VDC) and1H4-1H3 (27-36VDC)/ 1G4-1G3 (27-36VDC). Pulg back of 1C and 1H/1G connections.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 8/61

Start Up RoutinePack

.9

check (E/I-panel)LEDBAT-CHARGE MAINTENANCE

Fast charging/ Pre-charge qualification Maintenance charging Pre-chahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcrge qualification/ Fast charging/

Off On Blinking

Maintenance charging BAT-MODE SPBC_II/III supplied from controller

:The battery is charged by the SPBC_II/III. It must be connected at least for 8 hours (over night) before any operations are carried out. When the power of the system is switched off, the battery will be discharged due to the ongoing power demand from the SPBC_II.

switching off the unit for a longer period of time (&gt; 6h), please disconnect the battery and don't forget to re-connect afterwards!

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

.10

and SVT communication check (E/I-panel)

_OK

Bus available

://www.51wendang.com/doc/d18d862180e68ca57afad7bcr

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

.11

-EN check (E/I- panel: SPBC_II/III)

the proper inputs (use the LED indications located on SPBC_II/III)

/J INS DW

in the line voltage supply

mode

doors closed

Open Limit Door Open Button

the status of LED indication differs from the status listed in the table after power on, please check the circuits of the corresponding LED's.

-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 11/61

Start Up RoutinePack

Starting up in inspection4.1 Parameter Setup (GDCB): E/I- panel://www.51wendang.com/doc/d18d862180e68ca57afad7bcardocument 55661“Service Tool” and GAA30780DAG_Ins&amp;_IO for Reference to find the Parameter you should input before next step. Note:The version of the GDCB and GECB must be checked. The SCN must be as follow indicated or higher: GDCB --- AP230924CAE ( M-2-1-1) GECB --- GAA30780DAG (M-1-2-3) In order to enable normal run, the parameters must be setup according to the contract: All

in CONTRACT (M-2-3-1) All parameters in PROFILE (M-2-3-5)

:The below parameter should be kept as default: GDCB Parameter VelRate div 0..3 (M-2-3-2) must be 0; Any parameter in GDCB PROFILE (M-2-3-5) changed, must be sure actual installed LS length larger than the parameter of LS length min mm (M-2-1-7).

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 12/61

4.2

://www.51wendang.com/doc/d18d862180e68ca57afad7bcstem Start Up RoutinePack

Adjustment= LRT (Locked Rotor Test)

encoder calibration occures: On first run command, after drive power on Certain faults occuer After certain parameters changed

UP/DOWN

5~10 sec.

: During the calibration, a tone may be heard from the motor for a few seconds. This is normal and to be expected. No user intervention is required during the automatic calibration. Note that the adjustment is automatically repeated after certain faults are detected. This calibration occurred with dropped brake !

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 13/61

4.3

Start Up RoutinePack

of Run -Direction

Work Copyright&#169;XIZI OTIS Elevator Company

[此处http://www.51wendang.com/doc/d18d862180e68ca57afad7bc图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 14/61

4.4

Start Up RoutinePack

Brake Release check (E/I-panel)

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 15/61

55.1

Start Up RoutinePack

Reference System AdjustmentAdjust the limit switches Try to follow the table below to adjust the distance of the terminal switches. (Tolerance must be smaller than 20mm) The sign of a value is determined by the following rule: regard the leveling position of the elevator between the upper terminal floor and the lower terminal floor as reference, and marks somewhere on the rail to represent 00mm. For the top floor,‘ ’ means above the mark,‘-‘ means below the mark. For the grouhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcnd floor,‘ ’ means below the mark,‘-‘ means above the mark. Speed (m/s) 1.0 1.5 1.6 1.75 1LS/2LS -1000mm -1600mm -1800mm -2100mm 7LS/8LS 150 /-50mm 150 /-50mm 150 /-50mm 150 /-50mm

: 1. The 1LS/2LS distance is from drive calculation based on the acceleration&amp; deceleration is 0.6m/s2, you can verify the suitable distance by check the M-2-1-7-GOON LS min MM. 2. The distance indicated here is the distance of the terminal switch when the contact point opens, but not the one when the terminal switch presses the linkage.. 5.2 Adjustment of the photo-electric switch on car top and the hoistway leveling indicator plate The installation method&amp; dimensions of the car top photo-electric switch and leveling indicator plate for ACD2-MRL is shown below.

of bans: 250mm Number of bans: same as number of floor

Work Copyright&#169;XIZI

Elevator Company

[此处图片未下载成功]

ACD2http://www.51wendang.com/doc/d18d862180e68ca57afad7bc-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 16/61

Start Up RoutinePack

:1LV/2LV/UIS/DIS--normal open(NO) 5.3 5.4 Place some balance load into the car (about 45% of the car rated load). Adjust the positions of four leveling photo-electric switches (UIS: upper re-leveling photo-electric switch; 1LV/2LV: door-zone photo-electric switch; DIS: lower re-leveling photo-electric switch) Ensure they are vertical and separate from each other refer to the Fig., and make sure the order of the installation is UIS, 1LV, 2LV and DIS from top to bottom. 5.5 5.6 Operate the elevator to the leveling position of each floor. Adjust the leveling indicator plate on each floor and make the central line of the four photoelectric switches intercept with that of the plate. (It means the distance between the center line and 1LV/2LV is 30mm, and the distance between the center line and Uhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcIS/DIS is 100mm).This action will influence the leveling accuracy of the elevator.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 17/61

6

Start Up RoutinePack

of hoistway signals (PRS with RLEV/ADO)

: At short landings, the distance between door zones (=DZ vane) must be: 180 mm for normal speed up to 1,75 m/s 160 mm for normal speed up to 1,6 m/s - 130 mm for normal speed up to 1,0 m/s -

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 18/61

77.1

Start Up RoutinePack

Normal Running PreparationCheck the safety chain and doors chain Verify each safety switch of the safety chain is avhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcailable, and make sure each of them (OS, 8LS, 7LS, SOS, TES, PES, GS, DS, GSS) can stop the elevator under the requirements of inspection operation. (Attention: do not forget the availability of the lock of the landing door on the each floor.)

.2

the hoistway signals Run the elevator in the whole hoistway in inspection mode to check each hoistway signal, 1LV, 2LV, 1LS, 2LS, etc.. These signals can be checked by entering into M-1-1-2 of GECB, or by observing the status of LBDs in SPBC II/III.

.3

up of Door operator

start up the Door Operator please refer to the corresponding Field Installation Manual.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 19/61

88.1

Start Up RoutinePack

Learn RunStart up of hoistwayhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc learn run Note: During a learn run the door will close and will keep a torque.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 20/61

Learn run (continued)

Start Up RoutinePack

only when Load Weigh Type= 2 and Hitch LW calibration was confirmed.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 21/61

8.2

Start Up RoutinePack

during Learn Run When a fault is detected during the learn run, a corresponding message is displayed. After pressing&lt;GOON&gt;, the learn run is then aborted.Fault displayDrive NOT in CAN mode=&gt; abort&gt; DRIVE NOT READY&lt;SET&gt; aborts!&gt; No LS signals=&gt; abohttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcrt&gt; RUN IN PROGRESS=&gt; abort&gt; SIG NOISE/BOUNCE=&gt; abort&gt; PRS_SIG != 1VANE

The setup parameter Interface Type is not correct, should be a CAN controller. The drive is not yet ready to run. If this display appears for more than 1s the drive may be blocked by a fault. The CAN connection to the drive has been interrupted, no LS signal information has been received for&gt;2s. Learn Run start is attempted while car is running. Noise or excessive bouncing in hoistway signals (1/2LV, UIS, DIS). PRS sensors are on two vanes or on no vane when the actual learn run motion is about to start.

=&gt; abort&gt; TRANSITN OVERDUE Sensor transition on/off the vane does not occur when expected.=&gt; abort&gt; DETECTED## LDGs in 1LS: abort&gt;### LDGs before 2LS: abort&gt; INVAL PRS SIGNAL COMBI=&gt; abort&gt; 1LS: ON-&gt;OFF-&gt;ON gap=&gt; abort&gt; 2LS OFF-&gt;ON-&gt;OFF gap=&gt; abort&gt; 1LS/2LS OVERLAP!=&gt; ahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcbort&gt; VANE GAP SHORT: xxxxmm! abort&gt; LR ABORTED! see fault log&gt; LR ABORTED by ERO/TCI!&gt;

car leaves 1LS, the number## of encountered landings does not match the setup parameter According to the setup parameter, the top landing (###-) was reached before 2LS. Pattern of active and inactive PRS sensors is not possible on 1 or 2 vanes with the selected Vane Sensor Type. After leaving 1LS, the 1LS signal became active again=&gt; Gap in 1LS magnet/vane or bouncing in 1LS signal. After entering 2LS, the 2LS signal became inactive again=&gt; Gap in 2LS magnet/vane or bouncing in 2LS signal. 1LS and 2LS inputs are active at the same time. The gap between two vanes of xxxx mm is too short for the selected Vane Sensor Type. The Learn Run was aborted by a non learn run error. Look in the event log for detailed information. The Learn Run was aborted by switching to ERO or TCI.

.3

Bottom Landing Run The Fhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcind Bottom Landing run can be started via SVT menu 4-3 from any position in the hoistway. It positions the car in the bottom landing. This operation is required when starting a door sequence check run. In order to allow this run to establish valid position, a successful learn run must have been executed before.Unpublished Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 22/61

Start Up RoutinePack

user interaction during the Find Bottom Landing run and the preceding Start Dialog is same as Learn Run operation described above. 8.4 Viewing the Landing Table The landing table can be viewed in SVT menu 4-2. It shows each landing position and the learned vane length at each landing. The first landing is arbitrarily set to 10,0

mm. The display will look as shown below:

://www.51wendang.com/doc/d18d862180e68ca57afad7bclished Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 23/61

9Note:

Start Up RoutinePack

– Door Check Sequence (E/I-panel)

case of failure of a hoistway door contact, the car stops on this floor and is locked. An error message is shown. After elimination of all errors, the car has to be moved to the bottom landing first before starting the DCS RUN once again. Any change of parameter“TOP FLOOR” or“BOTTOM FLOOR” of GECB must restart DCS operation. Attention: The new feature Hoistway Access Detection (HAD) has been implemented to protect persons entering the hoistway and not properly following the safety instructions. If the DS contact is opened for longer than 4 seconds the GECB will go into HAD mode, the event“0306 HWY Access” is logged. The blinking message“Switch INS” appeahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcrs in the Status menu. The fault will not be cleared by switching the power off and on, the only way to bring the elevator back into normal operation is:  by ERO or  by pressing PES for at least 2 seconds.  by INS on TCI

: Please confirm SW6, SW7, SW8 on GECB board on ON position before DCS operation.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 24/61

Start Up RoutinePack

– Door Check Sequence (continued)

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 25/61

1010.1 10.2 10.3 10.4 10.5 10.6

Start Up RoutinePack

operationAccording to wiring diagram to examine the address of the remohttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcte site RS5 board whether they are dialed correctly and the wiring of the pin is right or not. Connect SVT to the SPBC_II/III, and use the SVT to call the elevator. Press M-1-1-1, then call the elevator to floor you want ((first floor is button‘0’, second floor is button‘1’ and so on). Press“Shift” and then“ENTER”, the elevator will land to the called floor. Check all the functions related to RS5&amp; RSEB Call the elevator in whole hoistway with SVT, and check speed displayed and check the drive state by SVT in the Emergency&amp; Inspection Panel.

11.1 11.2

AdjustmentPlace 45% of the duty load in car Call the elevator up run and down run, and check the motor current value by SVT (M-2-1-2) when car and counterweight are at a same level in hoistway. If the motor current is bigger when up run, should take out load form car; If the motor current is bigger when down run, should add load into car. Re-do the abovehttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc step until the motor current of up run and down run are almost same (&#177;0.3A).

.3 11.4

to above steps, adjust weight both in car and hoistway to achieve balance requirement of 4 7.5&#177;2.5%, After adjusting counterweight weight as above note, tighten counterweight screw.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 26/61

12 Final Adjustment12.1

Start Up RoutinePack

Level Adjustment

:  If the vanes are adjusted at a better manner at each floor, the car should stop correctly in each landing, otherwise the vanes should be adjusted accordingly. Then a new learn run is necessary.  The vanes must be centered on landing (due to UIS and DIS)

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图http://www.51wendang.com/doc/d18d862180e68ca57afad7bc片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 27/61

12.2

Start Up RoutinePack

Jerk, Rollback reduction

:  Before starting this adjustment, verify the proper working of the load weighing system.  And verify the parameter Balance% of GDCB set as the actual balance configuration.  And verify the parameter Inertia kg-m2 of GDCB set as correct calculation based on the contract configuration.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 28/61

12.3

Start Up RoutinePack

of ADO and RLV (Option)

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-http://www.51wendang.com/doc/d18d862180e68ca57afad7bc3-16 Page: 29/61

12.4

Start Up RoutinePack

for building configuration

:With the&quot;Allowed Mask&quot;, the building configuration (assignment of calls (car/ hall), cutting of landings (Cut Call), Card Reader, Parking, Ride profiles) is determined. An assignment is made for every landing. Rear doors are available, if on this landing the elevator may park and with which ride profile the elevator moves to the next landing. The key sequence (M-1-3-3-1) leads to the following&quot;Allowed Menu&quot;

.5

Indicator setup

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 30/61

Code Symbol 0 0 1 1 2 2 3 3 4 4 5 5 6 6 7 7 8 8 9 9

Start Up RoutinePackCode 10 11 12 13 14 15 16 17 18 19 Symbol (blank) A B (*) http://www.51wendang.com/doc/d18d862180e68ca57afad7bcC D (*) E F G (*) H I (*) Code 20 21 22 23 24 25 26 27 28 29 Symbol J (*) K (*) L M (*) N (*) O P Q (*) R (*) S Code 30 31 32 33 34 35 36 37 38 39 Symbol T (*) U V (*) W (*) X (*) Y (*) Z (*) * all segments

(*) for 16-segment position indicator and ELD only!

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 31/61

12.6

Start Up RoutinePack

test for code inspection

: When this test is activated, some functions are temporarily disabled or modified for several elevator runs: The check for proper brake switch state is disabled for 3 runs to allow the single-brake-shoe test - The vane input 1LS is disabled for one run to allow testing of the buffer. -

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-http://www.51wendang.com/doc/d18d862180e68ca57afad7bcMRL1.0~1.75m/s

.

: ACD2-M

_SUR_EN

: 2010-3-16 Page: 32/61

Start Up RoutinePack

PARAMETERS SETUP AND TROUBLE SHOOTINGDrive Key Parameters setupM-2-3-1 CONTRACT Interface Type Min 0 Max 1 Actual 1 Remark0= 422 Type 1= CAN Type

Type

-

A-402 Drive;25 OVFR1A-404 Drive;40 OVFR1A-406 Drive;60 OVFR2B-402 Drive;20 OVFR2B-403 Drive;30 OVFR2B-404 Drive;40

Type

-

/680@1m/s:101 800/1000@1m/s:203 630/680@1.5/6m/s:102 800/1000@1.5/6m/s/s:204 680@1.75m/s:204 800/1000@1.75m/s:204 ABA20220 AS1(Motor P/N):393 ABA20220 AS2(Motor P/N):395 ABA20220 AS3(Motor P/N):394 AAA20220BD Motor P/N):902, See appendix 1

Speed mm/s Rated rpm Inertia kg-m2

1 0.01 1

5000 9999.99 2

2

according to contract rpm on motor nameplate 1.5~5 Thihttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcs parameter stands for the type of ending of the encoder. 1 - single ended termination 2 - double ended termination

termintn 1/2

Type

. Specifies the type of encoder: 0– Incremental encoder 1– Sinusoidal encoder

PPR

-

or 4096, decided by encoder

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 33/61

Duty Load AC Main kg Vrms

Start Up RoutinePack10 50 16384 480 400Setup according to contract Use nominal AC mains, typically 400 for Europe.

*Load Weigh Type

– None 1 - LWB2 via CAN 2– Hitch LW CAN 3–Discrete LW via CAN

*Balance

%

mechanical overbalance matches paramhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bceter setting.

*Roping

..4

0

1

0

only at Load Weigh Type=20=PRS2CR with ADO/RLEV (1LV 2LV UIS DIS), 250mm magnets, minimum gap 110mm 1=PRS2CR without ADO/RLEV (1LV 2LV UIS DIS, but 2LV not passed to drive), 250mm magnets, minimum gap 140mm

*Vane Sensor Type

*DDP

2 0 0 Min 0

140 5 5 Max 1

0Setup according to contract Setup according to contract Setup according to contract

*Number of Stops *Bottom Landing *Landings in 1LS M-2-3-2 ADJUSTMENT Car Dir 0/1

0

Setup at jobsite (= 1 for most elevator configurations, not all)

Phase

/1

0 1

1 20

0 1

at jobsite

Phase 0/1 Start Gain Ot PU

to increase the responsiveness of the velocity control when load weigh sensor is not valid or not installed. A value of 1.0 essehttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcntially disables it. It can be increased to typical of 4.0. The maximum acceptable might depend on the system because it causes vibration problems as it is increased. However, it can be used for discrete load weighing sensors to decrease roll back.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 34/61

*End Gn Vel mm/s

Start Up RoutinePack0 0.1 50 0 0 0 Hz Hz 0 0 0 0 800 1 0.5 0 0 7 0 0 0 0 16000 1.5 150 500 1 2 300 300 50 3 2500 100 1 1 5 13 10000 7 20 40 2 0 1800 50 0.7 0 1.2 10 0 3 3 6Max duration of accel current= 167% of Rated mtr

Arms Use default (=0).

1 100 100 0.2 0.3Visible only when Motor Type= 901 or 902 Visible only when Motor Type= 901 or 902 Visible only when Motor Type= 901 or 902

Vel Resp PUPretorque Trim% *Track Error mm/s *Nhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bco Enc VThrs *No enc flt t sec Vel Notch1 Vel Notch2 PU

Band

div 0…3Cnv Notch Dc V BW Cnv BW Cnv Custom Hz Hz PU 0/1

Vmag Thrs PU*VaneBias (10) *Profile Delay mm ms

*Pos Stop Tol mm

Stop mm/secOverload sec

mtr i Arms Inv I Limit Cnv I Limit%%

0 0 100 0.01 0 Min 0

150 150 2000 50.0 1 Max 1 100 100 100 0.05 0 Actual 0

=60% rated accel current

Pick Time ms Pos Corr Lim mm

Tune

/1

-3-3 BRAKE *Internal Brk 0/1

0(OH-CONB604MRL) 0 or 1(ACD2-MRL)

*Brk Switch 0/1/2 Brk Pick Time ms

0

10000

1500

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 35/61

Brk Setl Time ms Lft Brk Delay ms Brk Lftd Dely ms M-2-3-4 Mhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcACHINE *Low Volt Op 0/1

Start Up RoutinePack0 0 0 Min 0 10000 10000 10000 Max 1 500 100 30 Actual Remark 0– Low voltage operation for

disabled. 1– Low voltage operation for

enabled. *Number of Poles *Rated Trq *Rated Trq I *Ld *Lq *R *T/A Slope *T/A Offset *Kt Slope Nm A mH mH Ohm% A 1/kNm A A mH/A mH/A mH 1/mA 1/mA^2 mH 2 0.1 0.1 0.01 0.01 0 0 0 0 0 0 0 0 0.01 0 0 0.01 1 0 Min 10 0 25 25 100 100 20000 1000 200 200 30 100 500 15 1000 1000 30 30 100 400 400 100 5000 40 Max 630 16000 1200 1200 2400 20 Actual 250 600 600 700Setup according to contract

0 0 15 0 0 0

*Id Saturation *Iq Saturation *Ld Slope *Lq Slope *Lq0 *Lq1 *Lq2 *Ld0

0

*Rated Motor rpm *Mag err thr eDeg M-2-3-5 PROFILE *Insp Speed mm/s

*Nom Speed mm/s *Accel *Decel *Jerk mm/s2 mm/s2 mm/s3

Work Copyright&#169;XIZI OTIS Elevator Company

://www.51wendang.com/doc/d18d862180e68ca57afad7bc[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 36/61

*Base Speed%

Start Up RoutinePack50 100 75

Key Parameters SetupParameter M-1-3-1-1 TOP BOTTOM LOBBY OPERATE Top floor Bottom floor Lobby position Operation FCL/ DCL/ SAPB 0 0 0 0 FCL (Full Collective) 1 DCL (Down Collective) PI-POS Type of Position Info for PI 0 0 Actual Floor 1 Next Commitable Floor HPI-POS Type of Position Info for HPI 0 0 Actual Floor 1 Next Commitable Floor LR-T Light Relay time 0 A parking car will switch off the car light after LR-T. The CPI-11 (ELD) is also switched off after this time. 0 (1) 255 seconds LR-MODE=0,1 0 (1) 255 minutes LR-MODE=2,3 if if Description Setting Remark

-MODE

/ Light Relay mode option

LR pulls after LR-T seconds only when door closed (Light) 1 LR pulls after LR-T seconds even if door is opened (Fahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcn) 2 LR pulls after LR-T minutes only when door closed (Light) 3 LR pulls after LR-T minutes even if door is opened (Fan)

-DIR

Fast Run Preferred Direction

Down 1 Up

-TYP

Type

Work Copyright

&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 37/61

LW-TYP

Start Up RoutinePackLoad Weighing Type 1 0 external via CAN (drive or LWB2 in the car) 1 external via CAN (drive with dynacell on the hitch) 2 discrete via RSL inputs in the car 3 same as external via CAN (hitch) but ANSL by Load from LWB is added (for ACD2, since DAB) 254 255 permanent OLD active disabled (OLD disabled

code tests) M-1-3-1-2 PKS-P PKS-DO Parking Service Position PKS default door 0 0 0 Both doors will open at PKS-P 1 Only front door ophttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcens 2 Only rear door opens DCP-T ANS Time until DCP-mode Anti Nuisance Service 50 1 25 (1) 255 s 0 Disabled&gt;0 Number of calls required to cancel all calls if car is loaded with ANS load (input: LWX) OLD-TYP Type of Overload handling 0 0 OLD-1 deleted) 1 OLD-2 ANS(kg) (car calls are remembered) upper limit for Anti Nuisance ANS LNS (%) OLD (%) M-1-3-1-3Unpublished Work Copyright&#169;XIZI OTIS Elevator Company

(car

(1) 250 kg

Limit for LNS load Lower Limit for OLD load

100

(1) 95% 100 (1) 110%

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 38/61

GRP-NO GROUP CNL CNL-MIN

Start Up RoutinePackCar identifier in group Number of cars in group Cars parking in Lobby Minimum Cars available to park CNL cars in Lobby M-1-3-1-4 DRIVE EN-ADO Drive type Enable Openinhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcg EN-ABL SPEED M-1-3-1-5 DOOR REAR EN-NDG Door type Rear door type Enable NDG (nudging) 12 12 0 13: with DOB 13: with DOB 0 1 NDG-T EN-CK Nudging Time Enable Cancel Doortime with CCB 20 00 disabled 1 enable CK 2 enable CBC 3 enable CK and CBC 4 enable CBC for Korea 5 enable CK and CBCK for Korea (DAE) note: CK= cancel doortime with

Advanced Door 1

:OVF40xR with ABL 0 1 disabled (XADO) enabled (ADO)

Brake lift Car speed

: disable

Enabled

button CBC= cancel registered car

with car button (press twice) CBCK for Korea= as CBC but also during run

-DW-D

delay

.Set to 0 when ADO or Releveing enabled;

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 39/61

Start Up Routinhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcePack2.Set to 10 when ADO or Releveing disabled

-C

Doortime Car

MIN-C and MAX-C. If door time is expired and DOB is still operated, this will increase the door time by 0.2 s at the next stop, otherwise door time is decreased by 0.2 sec MAX-C MIN-H MAX-H DTC-T DTO-T M-1-3-1-6 DZ-TYP EN-RLV Door Zone type Enable Releveling 1 1 0 Disabled 1 Enabled M-1-3-1-10 EN-CRT Door open floors quantity 0: up to 16 1: up to 32 2: up to 100 Max Doortime Car Min Doortime Hall Max Doortime Hall Door closing protect time Door opening protect time 40 20 40 20 20

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3

Page: 40/61

Start Up RoutinePack

://www.51wendang.com/doc/d18d862180e68ca57afad7bcCB Key Events descriptionSVT Display 100 Inv SW Oct E4 Description The magnitude of the inverter current exceeded an allowed threshold. Possible Causes&amp; Solutions Incorrect motor phasing→ change parameter错误！错误！未找到引用源。未找到引用源。. Shorted motor phase→ check motor wiring continuity. The fault threshold can be temporarily adjusted by the parameter错误！错误！未找到引用源。未找到引用源。. Applicable when错误！错误！未找到引用源。未找到引用源。= 0 or 1: OCT(A)= Drive I fullscale * Inv I Limit%* 0.9 * 1.05 (Drive I fullscale: 402 80A 404 110A) Applicable when错误！错误！未找到引用源。未找到引用源。= 2 or 3: OCT(A)= Drive I fullscale * Inv I Limit%* 0.9 * 1.25 101 Inv I Imbal E4 The sum of the three motor currents exceeded 10% full-scale current. Possible Causes&amp; Solutions Ground fault→ check there are no motor phases shorted to ground. Signal noise→ check that wiring guidelines are followed. 107 Inv Gate Flt E4 NOT applicable when错误！错误！未找到引用源。未找到引用源。 is 25A. An inverter IGBT gate supply voltaghttp://www.51wendang.com/doc/d18d862180e68ca57afad7bce fault was detected. Possible Causes&amp; Solutions Defective or shorted gate power supply→ change drive package (if occurs permanently).

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 41/61

108 Inv HW Oct E4

Start Up RoutinePackNOT applicable when错误！错误！未找到引用源。未找到引用源。 is 25A. For 60A V.2 - drives: The power section has detected a fault and set the discrete input (ERR1/INV_FLT: P1-12 ) to the GDCB. Because this input is shared by both HW Overcurrent and HW Overvoltage errors, the measured DC bus voltage is used to distinguish between them: - DC bus voltage is below a specified threshold --&gt; this fault was declared. - DC bus voltage is above a specified threshold --&gt; 116 Inv HW Ovt would have been declared. For all other drives except the 25A drive: The inverter currenthttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc exceeded a preset level, detected via hardware, (ERR1/INV_FLT: P1-12 ) to the GDCB. Possible Causes&amp; Solutions Incorrect motor phasing→ change parameter错误！错误！未找到引用源。未找到引用源。. Shorted motor phase→ check motor wiring continuity.

Overload

overload condition has been detected.

drive exceeded the

time allowed operating at the rated current of the motor. Possible Causes&amp; Solutions Excessive friction in system→ check for dragging brake or hoistway interference. The drive is undersized for the installed duty→ confirm system inertia. The fault threshold can be adjusted by the parameters:错误！错误！未找到引用源。,错误！错误！未找到引用源。未找到引用源。, and错误！错误！未找到引用源。未找到引用源。, but sho

not be increased by more than 10%. 110 Drive Limit W The drive is operating at its rated current limit.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75http://www.51wendang.com/doc/d18d862180e68ca57afad7bcm/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 42/61

111 No Id fdbk 112 No Iq fdbk E4

Start Up RoutinePackAn error has been detected with the current feedback of the inverter during magnetization of the motor at the beginning of the run. Possible Causes&amp; Solutions Open motor phase→ check motor wiring continuity. Bad current sensor→ return unit for service. See parameters错误！错误！未找到引用源。未找到引用源。 and错误！错误！未找到引用源。未找到引用源。.

Inv IPM Flt

only when错误！错误！未找到引用源。未找到引用源。 is 25A. Inicates a fault has been detected from the inverter Intelligent Power Module (IPM). Possible Causes&amp; Solutions Defective or shorted gate power supply→ change drive package (if occurs permanently). Incorrect motor phasing→ change parameter错误！错误！未找到引用源。未找到引用源。. Shorted motor phase→ check motor wiring continuity.

Inv HW Ovt

only for 60A V.2 drhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcives. The power section has detected a fault and set the discrete input (ERR1/INV_FLT: P1-12 ) to the GDCB. Because this input is shared by both HW Overcurrent and HW Overvoltage errors, the measured DC bus voltage is used to distinguish between them: - DC bus voltage is above a specified threshold --&gt; this fault was declared. - DC bus voltage is below a specified threshold --&gt; 108 Inv HW Oct would have been declared.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 43/61

200 Cnv SW Oct E4

Start Up RoutinePackThe magnitude of the converter current exceeded an allowed threshold. Possible Causes&amp; Solutions Defective hardware→ change drive package (if occurs permanently). The fault threshold can be temporarily adjusted by the parameter误！未找到引用源。未找到引用源。. Applicable when错误http://www.51wendang.com/doc/d18d862180e68ca57afad7bc！错误！未找到引用源。未找到引用源。= 0 or 1: OCT(A)= Drive I fullscale * Cnv I Limit%* 0.9 * 1.05 (Drive I fullscale: 402 80A 404 110A) Applicable when错误！错误！未找到引用源。未找到引用源。= 2 or 3: OCT(A)= Drive I fullscale * Cnv I Limit%* 0.9 * 1.25 NOT applicable when错误！错误！未找到引用源。未找到引用源。 is 25A. An inverter IGBT gate supply voltage fault was detected. Possible Causes&amp; Solutions Defective or shorted gate power supply→ change drive package (if occurs permanently).错

Cnv Gate Flt

Cnv HW Oct

applicable when错误！错误！未找到引用源。未找到引用源。 is 25A. The converter current exceeded a preset level, detected via hardware. Possible Causes&amp; Solutions Defective hardware→ change dr

package (if occurs permanently). Applicable only when错误！错误！未找到引用源。未找到引用源。 is 60A. A ground fault was detected on the converter. Possible Causes&amp; Solutions Ground fault→ disconnect drive from utility power and check that there are no phases http://www.51wendang.com/doc/d18d862180e68ca57afad7bcshorted to ground.

Cnv Gnd Flt

Bus Cap Fail

estimated power loss in the drive exceeded a limit. This indicates that excessive power is being dissipated in the drive and is a strong indication that a DC link capacitor has failed. The threshold for this fault is set bt the SVT parameters错误！错误！未找到引用源。未找到引用源。,错误！错误！未找到引用源。未找到引用源。, and错误！错误！未找到引用源。未找到引用源。

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 44/61

209 DC Link OCT S

Start Up RoutinePackApplicable only when错误！错误！未找到引用源。未找到引用源。 is 40A. Indicates excessive DC link current. Possible Causes&amp; Solutions Shorted motor phase→ check motor wiring continuity. Ground fault→ disconnect drive from utility power and check that there are no phases shorted to ground.

Cnv IPhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcM Flt

only when错误！错误！未找到引用源。未找到引用源。 is 25A. Inicates a fault has been detected from the converter Intelligent Power Module (IPM). Possible Causes&amp; Solutions Defective or shorted gate power supply→ change drive package (if occurs permanently). Defective IPM hardware→ change drive package (if occurs permanently). Ground fault→ disconnect drive from utility power and check that there are no phases shorted to ground.

Cnv Vmag Flt

, this fault occurs when power is removed from the drive AC input during a regenerative run. This fault may also occur in concert with This fault management is certain loss of safety chain events, but this should not be a concern (loss of safety chain causes an estop anyways). is lost during a regenerative run. If this fault occurs in such a way that interrupts normal elevator operation, then this condition should be reported, and the fault manahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcgement can be disabled by increasing the错误！错误！未找到引用源。未找到引用源。 parameter. This fault management is active only when the drive is regenerating and only when the nominal AC line voltage parameter错误！错误！未找到引用源。未找到引用源。 is set&lt;= 400. This fault management is not active when错误！错误！未找到引用源。 is set to 1. designed to protect other in-ciruit controller components when the AC line

DC Bus Over

DC bus voltage was greater than 108% of the nominal bus voltage of 750 VDC.Unpublished Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 45/61

301 DC Bus Under E6

Start Up RoutinePackThe DC bus voltage exceeded a limit. The limits are: For 415&lt; For未找到引用源。未找到引用源。. Vac&lt;= 480, limit= 70% of nominal (750). Vac&lt; 380, limit= 70% of nominal (750). For 380&lt;= Vac&lt;= 415, limit= 309 Vhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcdc. The nominal ac voltage is determined by the EEPROM parameter:错误！错误！

VAC Over

AC line voltage exceeded a limit. The limits are: For 415&lt; For找到引用源。找到引用源。. Vac&lt;= 480, limit= 112% of nominal. Vac&lt; 380, limit= 115% of nominal. For 380&lt;= Vac&lt;= 415, limit= 477 Vrms. The nominal voltage is determined by the EEPROM parameter:错误！错误！未

VAC Under

AC line voltage exceeded a limit. The limits are: For 415&lt; For找到引用源。找到引用源。. Vac&lt;= 480, limit= 85% of nominal. Vac&lt; 380, limit= 85% of nominal. For 380&lt;= Vac&lt;= 415, limit= 323 Vrms. The nominal voltage is determined by the EEPROM parameter:错误！错误！未

VAC Imbal 305 PLL Unlock

E

AC line input voltages differ from each other by more than 10%. The phase lock loop on the AC input voltage has unlocked. This is likely to occur when you try to run with a damaged IGBT. This fault sets the SAShttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc flag.

Single Phase

fault is declared when the drive is set to single-phase mode, and the T phase is connected to a live input. The power during single-phase operation should be connected to R and S phases only and the T-phase should be left open. See EEPROM parameter:错误！错误！未找到引用源。未找到引用源。

PLL Freq Rng

fault is declared when the drive ac line frequency estimate is outside of a frequency band specified by the parameter错误！错误！未找到引用源。未找到引用源。 for a amount of time specified by the parameter错误！错误！未找到引用源。未找到引用源。, while there is no PLL unlock fault. This fault is logged whenever the AC line is disconnected. Repeated logging may be an indication of a problem with the AC line.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 46/61

400 Brake http://www.51wendang.com/doc/d18d862180e68ca57afad7bcS1 SAS 401 Brake S2 SAS C4

Start Up RoutinePackThe indicated brake switch is in the wrong state. This is checked both when the drive is in the Idle state and when the drive is running. These faults result in complete the run fault response and set the SAS flag. Note: this event is also applicable when错误！错误！未找到引用源。未找到引用源。4 is set to 0 or 4 where constant states are required on BS1 and BS2 inputs. Possible Causes&amp; Solutions Incorrect parameter value→ verify correct value of错误！错误！未找到引用源。未找到引用源。. Incorrect brake switch wiring→ check brake switch wiring. Brake not lifting→ check brake wiring&amp; brake power supply. Insufficient time allowed→ see p

错误！错误！未找到引用源未找到引用源。引用源。 and错误！未找到引用源。未找到引用源。.

Brake Status

only when错误！错误！未找到引用源。未找到引用源。 is set to 0. The brake status feedback from the brake module is not in the correct state. Applicable only when错误！错误！未找到引用源。未找到引用源。 http://www.51wendang.com/doc/d18d862180e68ca57afad7bcis set to 0. One or both of the normally-closed BY contacts are not in the correct state. The BY relays should be energized when PTR is active, before the lift brake command is initiated. Possible Causes&amp; Solutions Incorrect wiring to brake module→ check brake module wiring. Incorrect brake power supply→ check brake power supply&amp; wiring. Adjust SVT parameter:错误！错误！未找到引用源。未找到引用源。

Brake BY

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 47/61

500 Overspeed E4

Start Up RoutinePackThe motor speed has exceeded a speed threshold. The speed threshold is determined by the operating mode of the drive: MCSS mode: CAN Normal: CAN Relevel: CAN Learn: CAN Rescue: adjustable perecentage of错误！错误！未找到引用源。未找到引用源。 110% of错误！错误！未找到引用源。未找到引用源。 fixed percentage of max http://www.51wendang.com/doc/d18d862180e68ca57afad7bcrelevel= 20 mm/sec fixed percentage of max learn= 500 mm/sec fixed percentage of max rescue= 300 mm/sec Manual Mode: adjustable percentage of错误！错误！未找到引用源。未找到引用源。

ERO/TCI: fixed percentage of错误！错误！未找到引用源。未找到引用源。 For MCSS and manual modes, the percentage is adjusted by SVT parameters:错误！错误！未找到引用源。未找到引用源。 and错误！错误！未找到引用源。未找到引用源。. 501 Pos Tracking E4 The position tracking error exceeded a threshold and indicates that the position feedback was not tracking the position reference from the profile generator. This fault is checked only when the drive uses its internal profile generator. See EEPROM parameter:错误！错误！未找到引用源。未找到引用源。 mm 502 Vel Tracking E4 The velocity tracking error exceeded a threshold. The velocity feedback was not tracking the velocity reference. Possible Causes&amp; Solutions Incorrect motor phasing→ change parameter错误！错误！未找到引用源。未找到引用源。. Wrong encoder feedback→ check encoder wiring and attachment. Incorrect paramethttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcer value→ verify correct value of错误！错误！未找到引用源。未找到引用源。. Excessive start jerk/ improper pre-torque→ verify load weigh device; if no load weigh device present (as during inspection), try increasing parameter错误！错误！未找到引用源。未找到引用源。 . See section错误！错误！未找到引用

源。未找到引用源。 for further instruction. Brake not lifting→ check brake wiring&amp; brake power supply. Hoistway obstructed→ check for obstruction (e.g. car or counterweight on buffer). The fault threshold can be adjusted by parameter错误！错误！未找到引用源。未找到引用源。. When Manual Mode is active, this fault threshold is automatically increased by a factor of 3.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 48/61

503 LRT Motion E4

Start Up RoutinePackThis fault indicates motion was detected while performing the Locked Rotor Test. The Locked Rhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcotor Test is performed at the beginning of the first run after a power-up to determine the position of the magnets when using a PM motor. set properly. The threshold for the fault is specified by the parameter错误！错误！未找到引用源。未找到引用源。. If the fault occurs, the brake may not be

Enc Pos Err

fault indicates that the drive has lost track of the magnet position when using a PM motor. This fault is necessary to prevent a loss of torque production. This fault may be caused by the encoder physically slipping with respect to the motor, or by a bad magnet position calculation during the locked rotor test (LRT). This fault is detected by comparing the magnet position, derived from the encoder and the result of the LRT, to the estimated magnet position based on the back-EMF of the motor. Since the estimator is back-EMF based, the fault detection is enabled only when the motor operates above 30% of the rated motor speedhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc. The default threshold for the fault is 20 electrical degrees. Another locked rotor test will be performed at the beginning of the next run to automatically re-determine the magnet position. See EEPROM parameter:错误！错误！未找到引用源。未找到引用源。 See EEPROM parameter:错误！错误！未找到引用源。未找到引用源。 See display parameter:错误！错误！未找到引用源。未找到引用源。

SPARE 506 Stopping Err

W

used. A time-out occurred because the stopping criteria at the end of the run were not satisfied. See EEPROM parameters:错误！错误！未找到引用源。未找到引用源。 and错误！错误！未找到引用源。未找到引用源。 Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Unexpected position at 1LS. The 1LS transition occurred at a position outside the expected range for 1LS, or the 1LS signal state is not consistent with hoistway position. Applicable only when landing table is valid and position is valid.

Pos at 1LS

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

http://www.51wendang.com/doc/d18d862180e68ca57afad7bcACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 49/61

508 Pos at 2LS NC

Start Up RoutinePackApplicable only for错误！错误！未找到引用源。未找

到引用源。 1. Unexpected position at 2LS. The 2LS transition occurred at a position outside the expected range for 2LS, or the 2LS signal state is not consistent with hoistway position. Applicable only when landing table is valid and position is valid. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Unexpected floor at 1LS. The 1LS transition occurred at a floor that is different from the expected floor. Applicable only when landing table is valid and limit switch signals are valid. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Unexpected floor at 2LS. The 2LS transition occurred at a floor that is different from the expected floor. Applicable only when landing table is valid and limit switch signals are valid. Applicable only for错误！错误！未找到引用源。未找到引用http://www.51wendang.com/doc/d18d862180e68ca57afad7bc源。 1. Both LS signals are valid and active simultaneously. This fault is used to decide if the NEXT COMMITTABLE fault response shall continue. If this fault is not detected with a certain time, or the fault“错误！未找到引用源。未找到引用源。” is not detected within a certain time, then the fault response is changed from NEXT COMMITTABLE to TIMED DECEL. If this fault persists at the end of a run, the drive will transition to (state, substate)= (IDLE AVAILABLE, RescueOnly). When the drive is in this substate, only commands for Rescue, ERO, ARO and MRO runs are accepted and LS are subsequently ignored. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Expected vane is missing. Logged only when outside a vane and an expected transition onto a vane has not occurred. Not checked in Inspection or Correction runs. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Expected transition is missing. Logged only when on a vane and an expected transition has not occurred. Not chhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcecked in Inspection or Correction runs.

Floor at 1LS

Floor at 2LS

1LS&amp; 2LS !

Missing Vane

3

No PRS Trans

3

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 50/61

514 Enc&lt;&gt; Vane NC 3

Start Up RoutinePackApplicable only for错误！错误！未找到引用源。未找到引用源。 1. An unexpected vane transition occurred. Possible causes could be: 1. Incorrect错误！错误！未找到引用源。未找到引用源。 setting. 2. Wrong错误！错误！未找到引用源。未找到引用源。 parameter setting. 3. PRS sensor signal wiring mistake. 4. PRS is having false transitions. 5. Encoder is not firmly attached to rotor. 6. Magnet has moved since it was learned during the learn run. 7. Belts are slipping or creeping over the drive sheave excessively. 8. Belts are stretchinhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcg excessvely. Applicable only for错误！错误！未找到引用源。未找到引用源。 1.

a normal run, the normal stopping profile did not decelerate the car in time to meet the target. The timed-decel is two-phased, containing a creep region. Only triggered at the terminal landings. The condition for triggering the fault is that the normal profile overshoots the target compared to a linear ramp-down of the speed at 110% of normal decel rate. Only triggered above a certain speed (presently 0.1 m/s). Applicable only for错误！错误！未找到引用源。未找到引用源。 1. A correction run missed the target. This fault is triggered when a correction run terminates outside of the limit switches or outside a vane, or at a different landing other than the terminal landing. The fault is logged after the car has stopped. Note: There is a minor bug with the SVT display for this fault. The fault response in the SVT is shown as ESTOP, when it is actually DECEL. Applicable only for错误！错误！未找到引http://www.51wendang.com/doc/d18d862180e68ca57afad7bc用源。未找到引用源。 1. Delayed Drive Protection (DDP) fault. The time between vanes has exceeded a specified value. It is not checked during ERO or TCI runs. The fault is cleared only by a power cycle or software reset of the drive. The time is specified by the EEPROM parameter:错误！错误！未找到引用源。未找到引用源。. This fault sets the SAS flag. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. Rollback of more than 5.0 mm at beginning of run

NTSD failed

Corr failed

DDP Error

Rllbck Start

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 51/61

521 Rllbck Stop W

Start Up RoutinePackApplicable only for错误！错误！未找到引用源。未找到引用源。 1. Rollback (reverse to direction of run) or overshoot (in direction of run) of more than 5.0 mm at ending of ruhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcn

Profile Err

profile chosen is not compatible with the system environment: The LS1 or LS2 lengths (learned during learn run) are too short for the drive to be able to stop within. This can be caused by too large speeds in the profile setting or too small deceleration entered. The other possibility would be a really short LS magnet. Cause A can be identified in the vane monitor M-1-7 by comparing measured LS to minimum required. The Nom Speed is set too high for the LS signal latency reported by the ICD of the GECB/TCBC (e.g. Nom Speed&gt; 1.8m/s with TCBC). This setting could lead to CORR runs not reaching the target vane.

No enc fdbck

fault indicates that the motor started moving without an encoder. This fault is triggered when the motor voltage exceeds a certain threshold defined by错误！错误！未找到引用源。未找到引用源。 while the encoder speed feedback is below 1mm/s. Check the integrihttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcty of the encoder. parameters. Also, check motor

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL

.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 52/61

530 No enc tmout E4

Start Up RoutinePackThis fault indicates that the drive started commanding velocity profile and the motor speed feedback did not exceed 1mm/s for the time duration defined by the parameter错误！错误！未找到引用源。未找到引用源。 (default value of the parameter is 0.4 secs). This fault detection is not active in Manual Mode. Possible Causes&amp; Solutions No encoder feedback signal→ check encoder wiring and mechanical attachment to the sheave. Incorrect parameter value→ verify correct value of错误！错误！未找到引用源。未找到引用源。,错误！错误！未找到引用源。未找到引用源。,错误！错误！未找到引用源。未找到引用源。, or any of the acceleration parameters in the (L)MCSS if operating in 422 mode. Excessive start jerk/ improper pre-thttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcorque→ verify load weigh device; if no load weigh device present (as during inspection), try increasing parameter错误！错误！未找到引用源。未找到引用源。 . See section错误！错误！未找到引用源。未找到引用源。 for further instruction. Brake not lifting→ check brake wiring&amp; brake power supply. Hoistway obstructed→ check for obstruction (e.g. car or counterweight on buffer). The fault threshold can be adjusted by parameter错误！错误！未找到引用源。未找到引用源。 Applicable only for错误！错误！未找到引用源。未找到引用源。 1. The transition into 1LS occurred with PRS signals that are not expected near the learned LS transition point. Applicable only when landing table is valid and limit switch signals are valid. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. The transition into 2LS occurred with PRS signals that are not expected near the learned LS transition point. Applicable only when landing table is valid and limit switch signals are valid. Applicable only when错误！错误！未找到引用源。未找到引用源。= 2 or 3. Applicable only when“AROhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc Type”= 2 (Interruptable ARO). This fault is declared when the motor speed has exceeded a speed threshold set by the parameter错误！错误！未找到引用源未找到引用源。 as a percentage of错误！未找到引用源。 . This fault is disabled with错误！未找到引用源。错误！未找到引用源。错误！未找到引用源。=0. If this fault is logged, the run is immediately terminated by the drive.

PRS Sigs 1LS

PRS Sigs 2LS

ARO Overspd

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 53/61

537 No EndRunCmd ER S

Start Up RoutinePackApplicable only for错误！错误！未找到引用源。未找到引用源。 1. While waiting for a DriveCommand EndRun in substate“

” the drive did not receive this command and timed out after 3s.. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. The run has been terminated with normally profiled decelerathttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcion by an OPB command (DriveCommand EndRun)..

Abort:EndRun

Decel Req Fl

to Interface Type= 3 only. A fault occurred and a timed decel is required, so a falsg is sent to the controller to request a timed-decel

Safety Chain

/ W

safety chain is not present. The opening of the safety chain will cause SX relays to drop, causing the drive to de-energized the motor and brake, thus causing an ESTOP. For 422 system, the response is ESTOP For CAN system, the response is LOG ONLY Note: Due to switch timing variation, this event can be logged sporadically when switching from NORMAL to ERO/TCI (no problem in unit)

E2 Invalid

data in the EEPROM is set to values incompatible with the current SCN or new EEPROM parameters have not yet been set. The invalid or blank values must be corrected. Pressing SHIFT_ENTER tells which parameterhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc is invalid and what menu it is located. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. The UIB and DIB inputs were not consistent with the run command from TCBC-type controller. This fault sets the SAS flag.

UIB DIB Err

Block by xxx

drive has been blocked from further runs. This occurs after certain critical faults have been detected, indicated by“S” in this table, or when certain faults have exceeded an allowed number of occurrences, indicated in this table by the number that follows the fault response category. The blockage must be cleared following the guidelines in Section错误！错误！未找到引用源。引用源。. This fault sets the SAS flag.

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 54/61

716 Illegal Cmd W

Start Up RoutinePackApplicable onlhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcy for错误！错误！未找到引用源。未找到引用源。 1 with systems using GECB where CarController ICD&gt;= 10, see“错误！错误！未找到引用源。未找到引用源。” in M-错误！错误！未找到引用源。未找到引用源。. An unexpected command has been received in a state where it could not be executed. It was ignored. Note it is possible that a GECB command coincides with a state change in the drive making execution of that command impossible. In such a case, this warning does not indicate a problem with the system. Applicable only for错误！错误！未找到引用源。未找到引用源。 1. CAN communication error detected. Applicable only for错误！错误！未找到引用源。未找到引用源。 1 and Load Weigh Type is set to 1 or 2. The drive has not received a loadweigh message within a certain time. The fault is cleared when a valid LW message is received. Applicable only fo

错误！错误！未找到引用源。未找到引用源。 1 and Load Weigh Type is set to 1 or 2. The drive received an erroneous value in the loadweigh message. Load Weigh Type= 1: The drive received the full scale value for load pehttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcrcent from the LWB2. The load percent value can be checked in the SVT menu of the LWB2. Load Weigh Type= 2: The drive received the full scale value for the hitch load measured in kg from the Hitch LW device. The value can be checked in the menu Monitor-Motion, it is the first value in the display“ HitchLW: Empty:“ The fault is cleared when a valid LW message is received.

CAN Err

LWSS Timeout

LWSS Bad Val

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 55/61

Start Up RoutinePack

Key Events Descriptionevent total runs minutes on class reason total number of runs since last power on minutes since last power on related setup -

System 0000 Timing 0001 S/W Reset W Task W Dummy task has not beenhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bc called within timeout. Software has been restarted. watchdog circuit on GECB was triggered. Software has been restarted. 0002 Illegal Int 0003 CanTxFull 0004 CanBusOff 0006 StackCheck 0007 SCN Error F W W W F illegal interupt was executed CAN messages cannot be sent CAN communication has been restarted Stack Violation was detected. Software has been restarted. Wrong Software. order a new software with correct partnumber. 0008 TimerSync F Internal updated restarted. 0009 Task Fail F Application software doesn't run properly. Software has been restarted. 0010 McbCommErr 0011 SpbCommErr 0012 Power On 0013 Event Fail 0014 PowerOffOn 0016 S/W Restart W Reset with unknown reason I W I Short Failure of PowerSupply. Board has been powered on. W No CAN connection to the SPB F No CAN connection to the drive software correctly. timers have not has been been -

Work Copyright&#169;XIZI OTIS Elevator Company://www.51wendang.com/doc/d18d862180e68ca57afad7bc

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 56/61

event 0017 Trace Error 0019 MissedLvInt

Start Up RoutinePackclass F reason bad value in the eventTraceControl buffer related setup -

and lv2 edge was missed

-

Control Sub System 0100 NAV OpMode F OCSS is not available due to drive fault (e.g. drive-fault (NR). This mode is also active after INS before the COR starts 0101 shutd. EPO W The car is not able to run during EPO (e.g. because it is switched to ERO); the next car is allowed to recover. 0102 DTC OpMode W door was not able to close (missing DCL, DFC or DW) within timeout NU (017) -

(018) NUSG (019) DCL (694) RDCL (695) DOOR, REAR DTC-T

DTO

was not able to open (missing DOL) within timeout

(000) RDOL (544) DOOR, REAR DTO-http://www.51wendang.com/doc/d18d862180e68ca57afad7bcT

DCP

was not able to answer a call within timeout (e.g. door was held open manually)

-T

PDS active 0107 DS bypass

F

door switch is opened Malfunction of Disable Door Switch Relays (DDSR) for Generic Firemen Service.

(784) DDSRC (970)

bypass

Service.

(971)

Relay (DEMERC) for Generic Firemen

Stuck DCB

Close Button contact permanent active

(003)

RDCB

Door Close Button contact permanent active

(547)

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 57/61

event://www.51wendang.com/doc/d18d862180e68ca57afad7bcarStart Up RoutinePackclass reason related setup

Control Sub System 0201 Correct.Run 0202/ES in FR 0203/ES in SR 0204 on 0205 SE-Fault F The car cannot start due to missing SE-signal Check the door bypass 0210/DZ in NST F DZ-signal was lost or not detected at all after having stopped 0211/DFC in FR 0212 SR 0213 DrvPrepErr W PrepareToRun expected from Drive (e.g. missing loadweighing information for ABL) 0214 DrvStuckPtr 0215 DrvStuckRtr 0216 DrvBrakeErr 0217 DrvCreepErr 0218 DrvShutdown 0219 DrvStartErr 0220 DrvService F W The drive requested“Request For Service” (REM). See drive event logging for reason. F The drive reports a Shutdown See event logging of MCB. F Drive Creeptime too long. F Brake not lifted. W Drive stuck in ReadyToRun(NoAbl) W Drive stuck in PrepareToRun/DFC in W W car door has been opened during Fast Run car door has been opened during Slow Run DZ-TYP TCI/ERO W W I I A correction run was http://www.51wendang.com/doc/d18d862180e68ca57afad7bcperformed (e.g. after INS, NAV) ES-input was activated during Fast Run ES-input was activated during Slow Run TCI or ERO has been switched on ERO-TYP -

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 58/61

event 0222 1TH-Fault

Start Up RoutinePackclass W reason The DBR-contact which is connected to the input 1TH is opened. The drive is powered down to allow cooling. related setup -

2TH-Fault

of the contacts which is connected to the 2TH is opened.

-

DrvEndRun 0225 dead 0228 on 1LS 2LS 110VAC

did not end the run.

-

VAC is dead for 5 seconds

-

switches 1LS and 2LS are active at the same time. Check power supply of the position reference system.

://www.51wendang.com/doc/d18d862180e68ca57afad7bc-

Chk

Adr

RSL I/Os have to be programmed to a valid address and are not allowed to be set to 00-0 or 01-0. Currently only one I/O is checked: 691– TCI Set I/O 691 to a valid address

(691)

PowerSave 0235 ABL Abort

drive package has been powered on

-D

Brake Lift was aborted because the door was not fully closed 10 seconds after the brake was lifted.

-ABL=1, DRV-TYP=1

/DW in FR

door has been opened during Run

-

/DW in SR

door has been opened during Slow Run

-

Control Sub System 0300 dfc_SE DBP: F While the door was opening or fully opened, the door bypass was found to be inac

(DFC low or SE high)Unpublished Work Copyright&#169;XIZI OTIS Elevator Company

-RLV, EN-ADO

[此处图片未下载http://www.51wendang.com/doc/d18d862180e68ca57afad7bc成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 59/61

event 0301 DCL in[]

Start Up RoutinePackclass F reason (R)DCL was active while the door was fully opened related setup DCL (694) RDCL (695) -

DoorBridge

or DFC was not low during the last door cycle, that means that the safety chain is bridged or the Door Bypass is defect.

on

:alw.

was active while the door was fully closed. This event is also logged when the fuses of the door system are burned. This event is not logged within the first 40 seconds after system startup.

(000)

Access

Door was opened or the car door is bridged. see description for blinking message 'Switch INS'

-

RDOL:alw.on

was active while the door was fully closed. Thihttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcs event is also logged when the fuses of the door system are burned. This event is not logged within the first 40 seconds after system startup.

(544)

sync

synchronization error

-

DOOR adr. 0310 chk 0311 chk 0312 Tout 0313 Tout RDOOR FDOOR RDOOR FDOOR

F

unused message origin Multidrop front door checksum error

-

rear door checksum error

-

front door communication timeout (&gt;200ms)

-

rear door communication timeout (&gt;200ms)

-

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 60/61

event 0314 noPull 0315 noDrop 0319 Ferror 0320 Rerror GSM GSM GDS GDS

Start Up RoutinePhttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcackclass F reason GDS relay not pulled related setup -

relay not dropped

-

input error Front door

-

input error Rear door

-

Sub System 0400 RSL parity W Two remote stations with the same address are connected to the same link 0401 RSL sync W Synchronisation lost on remote serial link. Check whether there is a shortcut on the link. 0402 RSL reinit F RSL driver has reported a problem. RSL was reinitialized. 0403 RSL Fail F Application has detected that the RSL driver doesn't run anymore. Software has been restarted. 0404 Hrtbeat RSL F RSL driver has detected that the application doesn't run anymore. Software has been restarted. 0405 RSL Board 0406 Group RSL F F RSL board mismatch! Group RSL has failed -

0500 RNG1 msg 0501 RNG1 time W W data error on Duplex/Triplex ring no ring messages received from other car for a specific thttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcime 0502 RNG1 sio 0503 RNG1 tx W W framing error on Duplex/Triplex ring ring messages couldn't be sent in an GROUP

timeUnpublished Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 61/61

event 0504 rxOff 0505 reset 0506 DES offline 0507 offline GCB RNG1 RNG1

Start Up RoutinePackclass W reason No messages are received within a timeout, and NO BREAK is

. W Reinitializing expired) F F DES is not present no GCB is present RING Service (stm_ring_run related setup -

0600 SPB-Alert W The Service Panel Board detected a -

which hinders a manual rescue operation with SPB and SDI. Possible reasons are: - defective speed encoders for SDI - defective E2PROM on SPB - Missing battery for SPB Press the SPB-buttons REB  DDO simultaneously to locahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcte the error. 0601 SPB:TempHTS 0602 LwssService 0604 Changed S/W I W W The Service Panel Board detected an SPB-Temp

. The LWSS requested“Request For Service” (REM). See LWSS event logging for reason. Informational event that new software was installed. The events are automatically cleared. No action necessary. -

S/W! 0606

subsytem software was installed that requires new GECB software.

-

SPB requested“Request For Service” (REM). See SPB event logging for reason.

-

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

ACD2-MRL1.0~1.75m/s

.

: ACD2-MRL_SUR_EN

: 2010-3-16 Page: 62/61

Appendix 1

Start Up RoutinePack

Tuning Data For AAA20220BD(Motor P/N) Series Machine MACHRATParameter Number of Poles Rated Trq Rahttp://www.51wendang.com/doc/d18d862180e68ca57afad7bcted Trq I Ld Lq R T/A Slope T/A Offset Kt Slope Id Saturation Iq Saturation Ld Slope Lq Slope Lq0 Lq1 Lq2 Ld0 Rated Motor Mag err thr LRT DC Level PU Units -Nm A mH mH Ohm% A 1/kNm A A mH/A mH/A mH 1/mA 1/mA^2 mH rpm eDeg --41T-53X1 14 300 16 52 90 0.8 37.4 4.8 0 3 16 0.9 0.5 75 0 0 60 330 20 0.1 8 41T-56X1 14 300 28 20 29 0.8 40 9.5 0 7 5 0.2 0.33 32 0 0 10 576 20 0.1 8 50T-56X2 14 420 36.2 15.5 20 1.6 39 11.6 0 5 5.3 0.17 0.18 22 0 0 10 576 20 0.1 8 50T-53X2 14 420 21.7 44 73 0.7 37 7.39 0 3.4 4 0.7 1 73.8 0 0 35.6 330 20 0.1 8

mot err eDeg

Work Copyright&#169;XIZI OTIS Elevator Company

[此处图片未下载成功]

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 https://www.51wendang.com/

亿万文档资料，等你来发现