GuideLed 11811 1-8h/D CGLine+ for surface-mounting parallel to wall

Pos.    )		ea.

Self-monitoring LED self-contained escape sign luminaire for wall surface-mounting, according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for systems according to DIN EN 50172, DIN VDE 0100-560 and DIN V VDE V 0108-100 for separate operation or for connection to the central monitoring facility CGLine+ Web-Controller (requires a non-shielded 2-core bus line).

Escape sign with LED Lightguide technology for especially homogeneous and

bright illumination of the pictogram acc. DIN 4844-1 and ISO 3864-1:

Lm >= 500 cd/m² (mains operation) for the white contrast colour and

Lm >= 200 cd/m² (mains operation) over the complete pictogram, uniformity Lmin/Lmax > 0.8.

LED-strip with high service life via optimised LED operating conditions and high luminous efficacy >100 lm/W for significantly reduced connected load. Easy connection via polarity reversal-protected wiring.

Slender design with low construction height of only 40mm including pictogram and mounting set.

Tool-free mounting of LED pictogram to the mounting set. Cable infeeds at rear, above and on side for mains and bus line, with additional space for cable routing.

Serial functionality:

- Emergency light operating duration settable at 1 h, 3 h or 8 h

- Dimmable in three steps (100%, 30%, 10%) with mains operation for use in dark ambient conditions

- Manual function test or duration test via testing button

- Test results with fault analysis (light sources, charging and battery circuit) and status displays

(Operation, function test, duration test) via 2-colour LED

- Automatic function test (weekly) and automatic duration test (every 6 months)

Can be optionally switched off with reminder of due duration test after 12 months

- Automatic charge monitoring and total discharge protection with switching lock

- No-load and short circuit monitoring

- 1 Minute switch-back delay to normal operation after mains return

- Blocking function via CGLine+ Web-Controller during idle operating times

- Generally suitable for maintained or non-maintained operation

Luminous flux (E/(N

at the end of the rated service time:		100% at 1 h, 50% at 3 h, 15% at 8h

Battery						LiIon 3.7V 2000 mAh

Viewing distance: 				30 m

Housing material: 				PC, PMMA

Housing colour: 				light grey RAL 7035

Connection terminals:				Through-wiring from mains L, L’, N, PE to 2.5 mm²

CGLine+ bus through-wiring to 1.5 mm²

Connection voltage:				220 - 240 V AC, 50/60 Hz

Connected load with mains operation:		5.3 VA / 4.7 W

Insulation class: 				II (protective earth required)

Protection rating: 				IP 20

Permissible ambient temperature: 		-5°C to +30°C (maintained mode)

0°C to +35°C (non-maintained mode)

Dimensions of LED pictogram (mm):		W = 327, H = 184, D = 13

Dimensions including wall mounting set:  	W = 327, H = 184, D = 40

3rd party certificate:				ENEC

Type: GuideLed 11811 1-8h/D CGLine+ for surface-mounting parallel to wall

Manufacturer: CEAG

GuideLed 11812 1-8h/D CGLine+ for semi-recessed mounting parallel to wall

Pos.    )		ea.

Self-monitoring LED self-contained escape sign luminaire for semi-recessed mounting in walls, according to DIN EN 60598-1, DIN EN 60598-2-22 and DIN EN 1838 for systems according to DIN EN 50172, DIN VDE 0100-560 and DIN V VDE V 0108-100 for separate operation or for connection to the central monitoring facility CGLine+ Web-Controller (requires a non-shielded 2-core bus line).

Escape sign with LED Lightguide technology for especially homogeneous and

bright illumination of the pictogram acc. DIN 4844-1 and ISO 3864-1:

Lm >= 500 cd/m² (mains operation) for the white contrast colour and

Lm >= 200 cd/m² (mains operation) over the complete pictogram, uniformity Lmin/Lmax > 0.8.

LED-strip with high service life via optimised LED operating conditions and high luminous efficacy >100 lm/W for significantly reduced connected load. Easy connection via polarity reversal-protected wiring.

Slender design with low construction height of pictogram of only 14mm.

Wall recessing housing for cavity walls, for accommodation of supply electronics and battery.

Serial functionality:

- Emergency light operating duration settable at 1 h, 3 h or 8 h

- Dimmable in three steps (100%, 30%, 10%) with mains operation for use in dark ambient conditions

- Manual function test or duration test via testing button

- Test results with fault analysis (light sources, charging and battery circuit) and status displays

(Operation, function test, duration test) via 2-colour LED

- Automatic function test (weekly) and automatic duration test (every 6 months)

Can be optionally switched off with reminder of due duration test after 12 months

- Automatic charge monitoring and total discharge protection with switching lock

- No-load and short circuit monitoring

- 1 Minute switch-back delay to normal operation after mains return

- Blocking function via CGLine+ Web-Controller during idle operating times

- Generally suitable for maintained or non-maintained operation

Luminous flux (E/(N

at the end of the rated service time:		100% at 1 h, 50% at 3 h, 15% at 8h

Battery						LiIon 3.7V 2000 mAh

Viewing distance: 				30 m

Housing material: 				PC, PMMA, sheet steel

Housing colour: 				light grey RAL 7035

Connection terminals:				Through-wiring from mains L, L’, N, PE to 2.5 mm²

CGLine+ bus through-wiring to 1.5 mm²

Connection voltage:				220 - 240 V AC, 50/60 Hz

Connected load with mains operation:		5.3 VA / 4.7 W

Insulation class: 				I

Protection rating: 				IP 20

Permissible ambient temperature: 		-5°C to +30°C (maintained mode)

0°C to +35°C (non-maintained mode)

Dimensions of LED pictogram (mm):		W = 327, H = 184, D = 13

Dimensions of wall recessing housing (mm):	W = 292, H = 112, D = 40

Wall cut-out 187 x 90

3rd party certificate:				ENEC

Type: GuideLed 11812 1-8h/D CGLine+ for semi-recessed mounting parallel to wall

Manufacturer: CEAG