本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.51wendang.com/doc/ecdebe501974f24dedd356c7

JOWA 3 SEP OWS Manual Rev A

防油类污染重要设备文件

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardJOWA OILY WATER SEPARATORJOWA 3SEP OWSALL MODELS: 1.0, 2.5, 5.0, 10.0m3/h STANDARD OPERATING INSTRUCTIONS AND TECHNICAL MANUALK:1-NYA K1-JOWA PRODUKTER3SEP1/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardTable of Contents 1.0 Introduction............................................................................................ 4 1.1 General ............................................................................................................. 4 1.2 System Overview.............................................................................................. 5 2.0 Technical Specification......................................................................... 6 2.1 Technical data for JOWA 3SEP OWS ................................................................... 6 3.0 Installation....................................http://www.51wendang.com/doc/ecdebe501974f24dedd356c7.......................................................... 8 3.1 Delivery ............................................................................................................ 8 3.2 Placement of the skid........................................................................................ 8 3.3 Pipe Connections .............................................................................................. 9 3.4 Separator Pump ................................................................................................ 9 3.5 Electric Connections....................................................................................... 10 3.6 Air Supply Pipes and Connections ................................................................. 11 3.7 Filter Media JOWA F - 200 C ........................................................................ 11 3.8 Quantity of Filter Media.....................................................http://www.51wendang.com/doc/ecdebe501974f24dedd356c7............................ 12 3.8.1 Filling the Tanks T2, T3 with Filter Media............................................ 12 3.9 Initial Start-up Checklist ................................................................................ 12 4.0 System Function.................................................................................. 13 4.1 Normal Flow Through the 3SEP OWS (See Flow Diagram)......................... 13 4.2 Manual Shut-off Valve Positions ................................................................... 14 4.3 Oil Release from 3SEP OWS (See Flow Diagram) ....................................... 15 4.4 Optional features on the 3SEP OWS.............................................................. 16 4.4.1 Bilge Clean Mode (Optional) ................................................................. 16 4.4.2 High Level Start Switch (Optional)........................................................ 16 4.4.2 Low http://www.51wendang.com/doc/ecdebe501974f24dedd356c7Level Stop Switch (Optional)......................................................... 16 4.4.3 Dry Running Protection (Optional) ........................................................ 16 4.4.4 Prime Water (Optional) .......................................................................... 16 4.4.5 3SEP OWS with JOWA Emulsion Breaking Unit EBU (Optional) ...... 17 5.0 Operation.............................................................................................. 18 5.1 General ........................................................................................................... 18 5.2 Start/Stop the 3SEP OWS .............................................................................. 18 5.2.1 Start/Stop Auto Mode............................................................................. 18 5.2.2 Start/Stop Bilge Clean Mode (optional) ................................................. 18 5.3 The PLC User Interface...http://www.51wendang.com/doc/ecdebe501974f24dedd356c7............................................................................... 19 5.3.1 Menu Display Tree ................................................................................. 20 5.3.2 Menu Display Tree Explanation............................................................. 21 5.3.3 When there is an alarm. .......................................................................... 22 5.4 The Oil Content Meter.................................................................................... 22 5.5 The Pneumatic Solenoid Control Valves ....................................................... 22 5.6 Oil Sensor CT03 ............................................................................................. 22 6.0 Maintenance......................................................................................... 24 6.1 Back flushing Procedure for Filter Tanks T2, T3.......................................... 24 6.2 Changinhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7g JOWA F - 200 C Filter Media in Filter Tanks T2, T3................... 25K:1-NYA K1-JOWA PRODUKTER3SEP2/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard6.2.1 Removing the Filter Media..................................................................... 25 6.2.2 Filling the Tanks T2, T3 with Filter Media............................................ 25 6.3 Checking the Anode Protection...................................................................... 26 6.3.1 Position of Anodes in the Tanks............................................................ 26 6.2 Regular Maintenance Timetable..................................................................... 27 6.2.1 Every day................................................................................................ 27 6.2.2 Every week .........................................................................................http://www.51wendang.com/doc/ecdebe501974f24dedd356c7.... 27 6.2.3 Every month ........................................................................................... 27 6.2.4 Every six months .................................................................................... 27 6.2.5 Every 12 months..................................................................................... 27 7.0 Trouble Shooting ................................................................................. 28 7.1 General ........................................................................................................... 28 7.2 Operation Errors ............................................................................................. 28 8.0 Flow Diagram (P &amp; I)............................................................................ 30 9.0 Mechanical Drawings .......................................................................... 31 10.0 Electrical Drawings and Pneumatic Drawings http://www.51wendang.com/doc/ecdebe501974f24dedd356c7.................................. 32 11.0 Oil Content Meter Operating Manual ................................................. 33 11.1 Rivertrace Alarm ............................................................................................ 34 11.2 Deckma Alarm................................................................................................ 35 12.0 1.0m3/h and 2.5m3/h Pump Operating Manual ................................. 36 13.0 5.0m3/h Pump Operating Manual ....................................................... 37 14.0 10.0m3/h Pump Operating Manual ..................................................... 38 15.0 Oil Sensor Operating Manual ............................................................. 39 16.0 Spare/ Consumables Parts List .......................................................... 40 17.0 Approval Certificates........................................................................... 41K:1-NYA http://www.51wendang.com/doc/ecdebe501974f24dedd356c7K1-JOWA PRODUKTER3SEP3/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard1.0IntroductionThe 3SEP OWS is a dual stage oily bilge water separation system designed to separate and remove free and emulsified oil. The system is available in four different capacities; 1.0m3/h, 2.5 m3/h, 5.0 m3/h and 10.0 m3/h. This manual contains the instructions for operating all four models. The treated water released by the 3SEP OWS contains not more than 15ppm oil in water. The system has been designed to meet the requirements prescribed by IMO MEPC 107 (49). For bilges with heavily emulsified oil in the bilge water a 3SEP OWS coupled to a JOWA EBU (Emulsion Breaking Unit) offers the best solution and ensures treated water under 5ppm. The 3SEP OWS is supplied standard with the necessary inlet for connecting a JOWA EBU. No further modifications are required to add a JOWA EBU.1.1GeneralTo http://www.51wendang.com/doc/ecdebe501974f24dedd356c7obtain all the advantages from operating a 3SEP OWS ensure that all users have adequate education for the equipment, ensure that the installation is correct and ensure that the 3SEP OWS is maintained and operated in accordance with the instructions in this manual. The correct function of the equipment cannot be guaranteed if the user fails to follow these instructions. Before installation and start-up read this manual carefully. Supplier and manufacturer: JOWA AB Tulebo 865 S-428 34 K&#229;llered , G&#246;teborg Sweden Phone:  46-31 726 54 00 Fax:  46-31 795 45 40K:1-NYA K1-JOWA PRODUKTER3SEP4/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard1.2System Overview.The 3SEP OWS is designed for a continuous flow with automatic operation, the system does not require any chemicals. The following text gives an overview of the 3SEP OWS separation process and the 3SEP OWS general arhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7rangement. The first stage removes the free oil by gravity with the help of coalescence plates. An adjustable oil sensor controls the pneumatic valve for automatic oil release to the sludge tank or any other dedicated tank. The adjustable oil sensor makes it possible to minimise the amount of treatable water released to the sludge tank. In the second stage emulsified oil is removed in the two filter tanks and the ppm value is monitored continuously by an oil content meter before the treated water is discharged overboard. The collected free oil on top of each filter tank is released automatically to the sludge tank at a preset interval. When a 15 ppm alarm occurs, the 3SEP OWS will automatically close the overboard line and re-circulate the treatable water to the bilge. When the contamination falls below 15 ppm the valve for overboard release will open again without human intervention. The system is designed as a compact skid assemblyhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 with all connection points collected, for easy “Plug n’ Play” installation. When the unit reaches the customer the only remaining thing to do is to connect water inlets and outlets and the electrical power supply, facilitating quick and easy installation onboard. Before leaving our workshop each unit has to pass a quality-test, where all functions are tested and checked. All equipment has the highest quality; the tanks are made of acid proof stainless steel, AISI 316L. Our pumps are supplied by internationally recognised brands. Spare parts are easily available from one of our offices or representatives worldwide.K:1-NYA K1-JOWA PRODUKTER3SEP5/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard2.0Technical SpecificationThis chapter contains a quick reference table with the main technical specifications for the 3SEP OWS. 2.1 Technical data for JOWA 3SEP OWSType: Capacity:http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 Influent: treated water oil content. Operation temperature: Operation Pressure: Volume (total): Weight (total): excl. Filter mtrl &amp; pump Total power consumption: Air supply: Tank material: Gaskets: Anode Protection: Tank volumes: Filter media: Filter media quantity: Type Approval Bilge Pump Type: Flow rate: Weight: Suction: Electrical data3SEP OWS-1 3SEP OWS-2.5 3SEP OWS-5 3SEP OWS-10 1 m&#179;/h 2.5 m&#179;/h 5 m&#179;/h 10 m&#179;/h Bilge water &lt; 15 ppm according to IMO MEPC 107(49) 5 - 55&#176;C Normal 0 – 2 Bar, Max 6 Bar. Safety Valve Protected. 225 L 225 kg (dry) 450 (wet) 1 kW 450 L 380 kg (dry) 830 kg (wet) 1 kW 900 L 520 kg (dry) 1420 kg (wet) 2 kW 2 250 L 842 kg (dry) 3092 kg (wet) 3 kW4 – 6 Bar Dry Instrument Air AISI 316L Nitrile Zinc Anodes installed on all tanks 3 x 75 L 3 x 150 L 3 x 300 L 1 x 500L (T1) 2 x 750L (T2,T3) 500 kgJOWA F - 200 C, supplied in 25kg Sacks 50 kg 100 kg 200 kgType approval by DNVhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7. Certificate No. P-11800 Mono Screw Mono Screw Pump Cgg Pump Cgh 1 m&#179;/h 2.5 m&#179;/h 21 kg 21 kg Max. 5.5 m lift capacity Sydex Xcenter Pump IS604 5 m&#179;/h 36 kg Sydex Xcenter BK039 10m&#179;/h 85 kgK:1-NYA K1-JOWA PRODUKTER3SEP6/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardVoltage: Frequency: Power consumption: R.P.M. Protection class: Thermal insulation class: 15 PPM Bilge Alarm Type:380 – 440 VAC 50 / 60 Hz 0.55 / 0.63 kW 0.55 / 0.63 kW 1.6 /1.55A 1.6 / 1.55 A 910 / 1100 910 / 1100 IP55 F1.5 / 1.74 kW 3.8 / 3.5 A 1380 / 14002.2 / 2.2 kW 4.9 / 4.5 A 1410 / 1690(See Operating Manual Chapter 12)K:1-NYA K1-JOWA PRODUKTER3SEP7/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard3.0InstallationThis chapter contains step-by-step information detailing how the 3SEP OWS is installed. At the end of the http://www.51wendang.com/doc/ecdebe501974f24dedd356c7chapter is a quick reference check list to aid in startup after installation or service. 3.1 DeliveryThe 3SEP OWS is delivered complete with all valves, pipes, necessary fittings and an oil content meter mounted on a single skid ready for installation onboard. The unit has passed a work-shop tested before delivery. 3.2 Placement of the skidThe 3SEP OWS skid should be placed on a plane surface and welded or bolted using the pre drilled holes in the skid. When installing the unit it is important to leave a minimum of 500mm working space in front of the unit (see mechanical drawings).K:1-NYA K1-JOWA PRODUKTER3SEP8/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard3.3Pipe ConnectionsAll connection points are collected together for easy “Plug n’ Play” installation: Capacity Piping Connections: Oily bilge water inlet: Oil release outlet (to sludge tank): Back flush water inlhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7et: Water outlet (overboard) Drain and Recirculate water (to bilge) Outlet to JOWA EBU (Optional) 3.4 1,0m3/h 2,5m3/h 5,0m3/h Male threads BSP as Standard Flanged (DIN, ANSI or JIS) as Option 1” - DN 25 1” - DN 25 1 &#189;” – DN40 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1” – DN 25 1 &#189;” – DN40 1” – DN25 1 &#189;” – DN40 1 &#189;” – DN40 1 &#189;” – DN40 10,0m3/h 1 &#189;” – DN40 1 &#189;” – DN40 1” – DN25 1 &#189;” – DN40 1 &#189;” – DN40 1 &#189;” – DN40Separator PumpThe pump is delivered as a separate unit for installation as close to the bilge water tank as possible to avoid suction problems. Use piping with the same dimension as the pump is designed for. Mono screw pump/ Sydex xcenter with Bspt female threading is standard. Use pipe connections according to specification below. Separator Size 1 m&#179;/h and 2,5 m&#179;/h 5 m&#179;/h and 10 m&#179;/h Dimension 1&qhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7uot; ( DN 25 ) 1&#189;” ( DN 50 )K:1-NYA K1-JOWA PRODUKTER3SEP9/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard3.5Electric ConnectionsThe electrical equipment of the separator is ready for installation when delivered. The power supply should be three phase 380-440 VAC 50/60Hz. Other power supplies on request. See the electrical drawings for further information. The mains supply should have a 10A fuse for separators up to 5m3/h and a 16A fuse for 10m3/h separators. Connect the main cable to terminal 1,2,3 in the main control box. Connect the pump motor cable directly over the current relay 2,4,6 in the main control box. Cable for pump, mains supply and 3 pole circuit breaker are not included in the delivery. Voltage: 3 phase 380-400-415-440-460-480 VAC 50/60 Hz.K:1-NYA K1-JOWA PRODUKTER3SEP10/41

: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OIhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7LY WATER SEPARATOR Standard3.6Air Supply Pipes and ConnectionsAir supply is connected to the pneumatic solenoid control valves. The connector is supplied for attaching of 6 mm Cu-pipe. The pressure should be 4-6 bar dry instrument air.Fig 3.6.1 Solenoid Block Location. 3.7 Filter Media JOWA F - 200 CFig 3.6.2 Air Inlet to Solenoids.The filter media, JOWA F – 200 C, for the filter tanks T2 and T3 is delivered fully prepared in sacks of 25 kilos each. The Separator is always empty by delivery. Filter media for the first filling is included in the delivery. NOTE! For guaranteed function we recommend the JOWA F - 200 C filter media.K:1-NYA K1-JOWA PRODUKTER3SEP11/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard3.8 ModelQuantity of Filter Media Tank Size 75 l 150l 300l 750l Quantity/Tank 50 kilo 100kilo 200kilo 500kilo1.0m3/h 2,5m3/h 5.0m3/h 10.0m3/h3.8.1 Fillhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ing the Tanks T2, T3 with Filter Media NOTE! Before filling check that the internal strainers are carefully fastened. Fill the tanks T2 and T3 through the upper hatches to 60-70 % of the tank volume, approximately 10-15 centimetres below the upper strainers. When the tanks are filled with filter media mount the upper hatches and back flush each filter one by one for at least 10 minutes until clean fresh water is coming through the sample valves V18 and V19 (See Chapter 6.1 for detailed back flushing instructions). Maintain low water pressure and speed during back flushing to avoid losing filter media from V18 and V19. Throttle V30 to control water speed and pressure during back flushing.3.9Initial Start-up ChecklistUse the following start-up checklist after installation or service. Fill tank T2 and T3 with filter media (See 3.8.1). Make sure the bilge pump is filled with water before start, to prevent running dry. Check that thhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7e manual valve positions on the 3SEP OWS are correct for normal operation (See Chapter 4.3) Open all valves between the bilge water tank and the separator. Open all valves on the separator discharge line. Back flush filter tanks 2 and 3 and make sure all carbon dust and other particles are removed from the new filter media (See Chapter 6.1). Turn the power on at switch S1. Check rotation of the pump Now the separator is ready for normal operation.K:1-NYA K1-JOWA PRODUKTER3SEP12/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard4.0System Function.This chapter provides a detailed description of the unique functions of the 3SEP OWS. The material provided in this chapter gives the operator the possibility to gain an excellent understanding into how and why the 3SEP OWS performs its functions. It is intended that the information in this chapter may be used to help the operatohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7r optimise the 3SEP OWS performance to his or her specific bilge requirements. 4.1 Normal Flow Through the 3SEP OWS (See Flow Diagram)Normal flow through the 3SEP OWS occurs in Auto Mode. In auto mode the separator consists of three (3) tanks connected in series, tanks T1-T3, and the oil content meter. Tank T1 utilises specific gravity and coalescence effect to separate and release free oil. Tanks T2 and T3 are filters utilising the filter media JOWA F - 200 C to remove the majority of the remaining emulsified oil. Finally the oil content of the treated water is checked by the oil content meter before it is discharged overboard. The bilge water is initially pumped into the top of T1 thru valve V10 where most of the free oil is gathered on the coalescence surfaces. When the oil senor CT03 detects oil it is released through the pneumatically controlled valve V01 and is delivered to the concentrated sludge tank. The partly treated wathttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7er is then pumped out of the bottom of T1 through the two filter tanks T2 and T3 connected in series. The pneumatically controlled valves V02 and V03 release the free oil at the top of T2 and T3 to the concentrated sludge tank. At the outlet of tank T3 the oil content in the treated water is checked by the oil content meter. The valves V21 and V22 shall be in open position and the valve V20 shall be throttled (partly closed) to force a part flow through the oil content meter. The treated water flows through the pneumatically controlled valve V04 for overboard discharge. NOTE! It is very important that the valve V20 in between the filter tank T3 outlet and the discharge of clean water is throttled (partly closed) to obtain flow through the oil content sensor.K:1-NYA K1-JOWA PRODUKTER3SEP13/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardIf the oil content of the flow cominghttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 from the outlet the 3SEP OWS exceeds 15ppm the pneumatically controlled valve V04 closes and the pneumatically controlled valve V05 opens, re-circulating the discharge from the 3SEP OWS to the bilge. When the oil content detected by the oil content meter falls below 15ppm again V05 will close, V04 will open and overboard discharge will resume. The recirculation cycle occurs for 20 minutes and is adjustable (See Chapter 5). If the treated water remains above 15ppm at the resumption of normal flow after the recirculation cycle, the 3SEP OWS will stop and an alarm will occur. The 3SEP OWS can be back flushed and restarted. See Chapter 6.1 for back flushing instructions. 4.2 Manual Shut-off Valve PositionsThe following tables indicate which of the manually controlled valves are open, closed and Throttled (Partly Closed) during normal operation of the 3SEP OWS. Opened V10 V21 V22 Closed V11 V12 V13 V14 V15 V16 V17 V18 V19 V23 V30 Throthttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7tled (Partly Closed) V20K:1-NYA K1-JOWA PRODUKTER3SEP14/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard4.3Oil Release from 3SEP OWS (See Flow Diagram)Oil Release occurs at three points on the JOWA 3SEP OWS; T1, T2 and T3. The released oil should be delivered to a suitable tank such as the concentrated sludge tank. The flexibility of the 3SEP OWS oil release system allows a high degree of control over the oil release. In the first stage, tank T1, oil release is controlled by an oil sensor, CT03. The sensitivity of the oil sensor CT03 is operator adjustable in order to minimise the amount of treatable water released from T1. To adjust the sensitivity of the oil sensor CT03 see chapter 5.3 and 5.6. The oil accumulates in the top of T2 and T3 as the partly treated water is delivered from T1. Oil release from the filter tanks T2 and T3 occurs automatically. This oil is relhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7eased by the pneumatically controlled valves V02 on tank T2 and V03 on tank T3. The time length interval between oil releases for V02 and V03 is fixed. Oil is released from V02 every five minutes, for a time period of 20 seconds. Oil is released from V03 every hour for a fixed period of 5 seconds. When the JOWA 3SEP OWS is started an automatic oil release from V01, V02, and V03 occurs for a fixed period of 10 seconds. This ensures that the pure oil that has gathered at the tops of the tanks while the unit has been stationary is now released.K:1-NYA K1-JOWA PRODUKTER3SEP15/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard4.4Optional features on the 3SEP OWS.The following are optional features for the 3SEP OWS: 4.4.1 Bilge Clean Mode (Optional) Bilge clean mode gives the operator the flexibility to run the 3SEP OWS while docked in the harbour. In bilge clean mode no treathttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ed water is released overboard but constantly re-circulated to the bilge. In bilge clean mode the flow from the bilge only passes through the first stage tank T1 and then returns to the bilge tanks. The bilge water is pumped into the top of T1 thru valve V10 where most of the free oil is gathered on the coalescence surfaces. When the oil senor CT03 detects oil it is released through the pneumatically controlled valve V01 and is delivered to the concentrated sludge tank. The flow then passes through V13 and returns to the bilge. Running in bilge clean mode allows the maximum amount of free oil to be removed from the bilge water before it passes through the filter tanks T2 and T3, maximising the life of the JOWA F - 200 C filter media. 4.4.2 High Level Start Switch (Optional) Automatically starts the 3SEP OWS when the bilge water level is high, using a level switch located in the bilge tank. 4.4.2 Low Level Stop Switch (Optional) Automhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7atically stops the 3SEP OWS when the bilge water level is low, using a level switch located in the bilge tank.. 4.4.3 Dry Running Protection (Optional) Protects the 3SEP OWS pump from running dry. 4.4.4 Prime Water (Optional) Automatically primes the 3SEP OWS pump.K:1-NYA K1-JOWA PRODUKTER3SEP16/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard4.4.5 3SEP OWS with JOWA Emulsion Breaking Unit EBU (Optional) A JOWA EBU system may be coupled to the 3SEP OWS as an extra treatment stage. The JOWA EBU 3SEP OWS package can achieve treated water with less than 5ppm oil in water. It is strongly recommended that the operator consider a 3SEP OWS coupled with JOWA EBU if the bilge water contains high levels of emulsified oil. The JOWA EBU is a chemical treatment of the emulsified oil in water. The chemical is a flocculent that helps the small particles of oil coalesce together and thus http://www.51wendang.com/doc/ecdebe501974f24dedd356c7separate by gravity. The 3SEP OWS skid is ready supplied with the connection for a JOWA EBU (See Flow Diagram). The adding a JOWA EBU requires no additional input from the operator other than to connect the JOWA EBU to the Optional JOWA EBU outlet on the 3SEP OWS skid. No further modifications are required to add a JOWA EBU.Fig 4.4 JOWA EBUK:1-NYA K1-JOWA PRODUKTER3SEP17/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard5.0OperationThis chapter gives the operator detailed information on how the major control components of the 3SEP OWS are operated and adjusted. 5.1 GeneralGeneral operation of the 3SEP OWS is facilitated by the PLC user interface and the switches located on the door of the main control box. All of the electric and pneumatic control equipment is located on the control cabinet stand at the side of the 3SEP OWS skid frame. Before delivery all electrical http://www.51wendang.com/doc/ecdebe501974f24dedd356c7equipment on the unit is connected and thoroughly work-shop tested.   All electric equipment is connected to the main control box and the 3SEP OWS is operated from here. The main power switch, S1, for the 3SEP OWS is located on the side of the main control box.   The electronic parts for the oil content meter are located inside the oil content meter control box.   The pneumatic solenoids for the pneumatic control valves are located on the side of the 3SEP OWS skid frame control stand 5.2 Start/Stop the 3SEP OWSAfter the actions in section 3.9 ‘Initial Start-up Checklist’ have been completed the unit can be started and run in normal operation. 5.2.1 Start/Stop Auto Mode Turn on switch S0, ‘power on’. Turn switch S2 to position 1 for auto mode. The 3SEP OWS will run in auto mode. The 3SEP OWS first runs through a start routine before normal flow commences. In the start routine oil is released from all tanks by means of the pneumaticahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7lly controlled valves V01-V03 opening for a short period. To stop the 3SEP OWS simply switch S2 to position 0. 5.2.2 Start/Stop Bilge Clean Mode (optional) Turn on switch S0, ‘power on’. Turn switch S2 to position 2 for bilge clean mode. The 3SEP OWS will run in bilge clean mode. To stop the 3SEP OWS simply switch S2 to position 0.K:1-NYA K1-JOWA PRODUKTER3SEP18/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard5.3The PLC User InterfaceThe PLC user interface facilitates the running and understanding of the 3SEP OWS. Through the user interface and display on the main control cabinet door you receive all messages concerning the 3SEP OWS such as alarms, and preset times.Display WindowLeft/ Right KeysUp/ Down KeysEnter KeyFig 5.3 PLC InterfaceThe user moves up and down through the menu display tree using the up/down and left/right keys. Information such as time ihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7s input using the number keys. The input value is confirmed by pressing the enter key.K:1-NYA K1-JOWA PRODUKTER3SEP19/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard5.3.1 Menu Display Tree The following schematic shows how the user navigates through the menus in the 3SEP OWS. Numbers are displayed where the # appears 1.02.03.03.14.04.14.2Fig 5.3.1 Menu Display TreeK:1-NYA K1-JOWA PRODUKTER3SEP20/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard5.3.2 Menu Display Tree Explanation Menu 1.0 2.0 3.0 SubMenu Function/Description Start-up display. User sets the time here 3SEP Operational Status. Displays Run or Stop. Tank T1 oil release Display. The SV value is set by the user in sub menu 3.1, and the value PV is the real time value sensed by CT03. The user presses enter to go to 3.1 where SV is input Thhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7e desired SV Oil Release value 0-100 (See 5.6) is input here. Press enter to exit sub menu 3.1 Timers Menu. Press right arrow key to enter sub menus Adjust re-circulation time here, factory value is 20mins, (see Chapter 4, Sect 4.1). Navigate back to menu 4.0 or down to sub menu 4.2 using the up/down left/right keys Optional extra (With Dry Running Protection)3.1 4.0 4.1 4.2K:1-NYA K1-JOWA PRODUKTER3SEP21/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard5.3.3 When there is an alarm. There are two alarm conditions. Over-current alarm or Re-circulation alarm if time has run out while the ppm value is above 15. When an alarm occurs the following information will be present: 1 2 5.4 Failure message indicates the problem. When the failure is corrected the alarm can be reset by pressing the red reset button. The Oil Content MeterThe oil content meter is located on the controlhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 cabinet stand on the 3SEP OWS skid. The oil meter door displays the oil content in PPM in the water being discharged from the 3SEP OWS. The alarm limit for the oil content is adjustable between 0 - 15 PPM. The oil content in the water is measured by the sensor unit located to the right of the oil meter electric control box. To obtain a flow through the sensor unit the valve V20 must be throttled (partly closed). If there is no flow through the oil content meter the reading will be corrupt and the oil content meter will register an alarm. A complete Technical and Operation manual for the Oil Content Senor will be included in chapter 12 of this manual.5.5The Pneumatic Solenoid Control ValvesThe pneumatic solenoid control valves control the valves V01 to V05. Each pneumatic solenoid control valve is marked with the valve position number. The air pressure to the solenoid control valves must be 4-6 BAR dry instrument air to get a phttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7roper function and performance of the valves.5.6Oil Sensor CT03The oil sensor, CT03, measures the conductivity between the sensor rod and the pipe wall. The sensitivity-index of the oil sensor varies from 0 to 100, where 0 is pure oil and 100 is water (air also has a value of 0). The factory set sensitivity value is 80.K:1-NYA K1-JOWA PRODUKTER3SEP22/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardThe sensitivity of CT03 may be adjusted by the operator to suit the amount of free oil in the bilge water. For example a lower sensitivity value on CT03 may suit a bilge with high amounts of free oil. Lowering the sensitivity value has the advantage of decreasing the amount of water released to the concentrated sludge tank. However lowering the value may also shorten the lifespan of the JOWA F – 200 C filter media, as it must absorb more oil. Conversely, raising the value whttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ill result in more water being released to the concentrated sludge tank but a longer filter media lifespan. The sensor rod has to be cleaned regularly to ensure its correct function, See chapter 6 for cleaning instructions.K:1-NYA K1-JOWA PRODUKTER3SEP23/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard6.0MaintenanceThis chapter provides detailed instructions for common maintenance operations on the 3SEP OWS. A regular maintenance timetable is also included. The timetable is designed to aid the operator in scheduling minor periodic maintenance tasks thus avoiding unnecessary breakdowns. 6.1 Back flushing Procedure for Filter Tanks T2, T3.It is necessary to back flush the filter tanks T2 and T3:       After JOWA F - 200 C is installed at start-up The oil content meter gives an alarm indicating an oil content exceeding 15 ppm for a period of extended time or After changhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ing the JOWA F - 200 C filter media as part of regular service.Proceed as follows: 1. Switch off the unit, close the valve V10 (and V11 if 3SEP OWS is connected to a JOWA EBU). 2. Make sure that the pressurised fresh water is available at the valve V12 3. Start the back flushing of filter tank T2 by opening the valve V12. 4. Open valves V15 and the 3-way valve V30, carefully monitor the pressure. Do not fully open V30 immediately, open it slowly, allowing the flow to build pressure slowly. This avoids flushing away the JOWA F - 200 C filter media from the sample points V18 &amp; V19. It also avoids damage to the pneumatic and non-return valves from flushing the JOWA F - 200 C filter media into them. 5. Be sure that V30 is allowing the flow to pass thru T2. You may check this by observing the outlet pressure at V18 6. Check the water quality through the valve V18. 7. Back flush until the water is clean (5-10 minutes for each filter)http://www.51wendang.com/doc/ecdebe501974f24dedd356c7. 8. Close the valves V12 and V15 and V18. 9. Start the back flushing of filter tank T3 by opening the valve V12 and then valve V16 and the 3-way valve V30. Again, Do not fully open V30 immediately, open it slowly, allowing the flow to build pressure slowly. 10. Be sure that V30 is allowing the flow to pass thru T3. You may check this by observing the outlet pressure at V19 11. Check the water quality through the valve V19. 12. Back flush until the water is clean (5-10 minutes for each filter). 13. Close the valves V12 and V16 and V19. 14. Back flushing is complete.K:1-NYA K1-JOWA PRODUKTER3SEP24/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard6.2Changing JOWA F - 200 C Filter Media in Filter Tanks T2, T3.The filter media must be changed at least every 12 months. This section describes the procedure for changing the filter media. 6.2.1 Removing the Filter Media NOTE! Whttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7hen removing filter media, make sure that you do not damage internal filter tank strainers. The strainers are located in the top and bottom of T2 and T3, see mechanical drawings chapter 9.   Stop the 3SEP OWS at the main control box, close V10 (and V11 if 3SEP OWS is connected to a JOWA EBU).   Open the filter tanks bottom valves V15, V16 and V14 to drain the water from the filter tanks.   Open the sample valves V18 and V19 to let air into the top of the tanks.   Remove the upper hatches and wait until the water flow at the bottom has stopped.   Open the lower hatches and empty the tanks of filter media. Clean the tanks carefully inside and check that the internal strainers are undamaged and free of carbon and oil. Check the zinc anodes and change them if more than 70 % of the zinc has corroded. 6.2.2 Filling the Tanks T2, T3 with Filter Media NOTE! Before filling check that the internal strainers are carefully fastened and undamagedhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7. Should the strainers be damaged Spare/Consumables Parts List. replace them. See chapter 17Fill the tanks T2 and T3 through the upper hatches to 60-70 % of the tank volume, approximately 10-15 centimetres below the upper strainers. When the tanks are filled with filter media mount the upper hatches and back flush each filter one by one for at least 10 minutes until clean fresh water is coming through the sample valves V18 and V19 (See the previous section of this chapter for detailed back flushing instructions). NOTE! For guaranteed function we recommend the JOWA F - 200 C filter media.K:1-NYA K1-JOWA PRODUKTER3SEP25/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard6.3Checking the Anode ProtectionThe first stage tank, T1 and the filter tanks T2, T3 are made of acid proof stainless steel AISI 316L. The tanks are protected against corrosion by fixed zinc anodes. The zihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7nc anodes should be checked every six (6) months. They should be changed if more than 70% of their mass is corroded 6.3.1 Position of Anodes in the Tanks.Tank T1: For all sizes 1.0 – 10.0m3/h the zinc anode is located at the front of the tank in the lower socket. The front of the tank, T1, can be considered to be under the main control cabinet Tanks T2, T3: 75 l tank (1.0m&#179;) 150 l tank (2,5-5m&#179;) 300 l tank (5m&#179;) 750 l tank (10 m&#179;) inside lower hatch inside lower hatch inside lower hatch inside lower hatchThe location of the anodes are marked with labels.K:1-NYA K1-JOWA PRODUKTER3SEP26/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard6.2Regular Maintenance Timetable6.2.1 Every day     Check that the pneumatic solenoids and valves are functioning properly Check for leaks of both air and oil/water6.2.2 Every week     Back flush the filter tanks T2http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 and T3 according to the instructions in 6.1. Clean the oil content meter measuring cell by pushing down the manual plunger several times. The plunger is located on the top of the oil content meter6.2.3 Every month   Check the Oil sensor CT03 and adjust according instruction chapter 5.6 if necessary. Clean the rod of the oil sensor thoroughly by unscrewing and removing CT03 from T1.6.2.4 Every six months     Check the zinc anodes in tanks T1, T2 and T3 Check the Rotor at the pump P01.6.2.5 Every 12 months     Change filter material in the filter tanks T2 and T3 and clean the inside of the tanks. Clean tank T1 on the inside. Remove the oil release flange and pipe and clean the tank thoroughly using high pressure hot water to remove the oil.K:1-NYA K1-JOWA PRODUKTER3SEP27/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard7.0Trouble ShootingThis chapter provides the ohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7perator with a comprehensive trouble-shooting guide. 7.1 GeneralEvery error in the operation is indicated as an alarm and presented at the operators display of the PLC.7.2Operation ErrorsError The oil content meter indicates over 15 PPM The pump, P01, does not give a flow.  Remedy/Action Back flush the filter tanks T2 and T3. Replace the JOWA F - 200 C filter media if necessary Check the Rotor and replace it if necessary. Check that the electric motor is receiving the right voltage. Check the rotation of the pump Check that the manual valves in the flow direction are opened. Check that air is connected. Run the pneumatic valves manually by turning the small screws on the solenoid control valves. Check the connectors for the valves for air leaks. Back flush the tanks T2 and T3   Pressure too high at the pressure gauge P01 and the safety valve V50 opens.         K:1-NYA K1-JOWA PRODUKTER3SEP28/41

://www.51wendang.com/doc/ecdebe501974f24dedd356c7arDate: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR StandardError The pneumatic valves do not open.    Remedy/Action Check the air connection (4-6 bar). Test run the pneumatic valves manually by turning the small screws on the solenoid control valves. Check the connectors for the valves for air leaks. Check the plastic hoses. K:1-NYA K1-JOWA PRODUKTER3SEP29/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard8.0Flow Diagram (P &amp; I)K:1-NYA K1-JOWA PRODUKTER3SEP30/41

D

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard9.0Mechanical DrawingsK:1-NYA K1-JOWA PRODUKTER3SEP31/41

654321DD1834C785 6601784C535410285 16080910 760375BB950 1188FILE NAMEADRY MASS: 260,02 kg WORKING PRESSURE: 2 BAR MAINTENANChttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7E AREA: 500mm PERIMETER IN FRONT OF UNIT COMPLIES WITH MARPOL IMO MEPC 107(49)24-0010-01-01 3Sep 1m3.iam A3 Greg Shannon DRAWN 2004-09-17CHECK APPR. REVSIZEMODEL ID24-0010-01SCALE1:15GA, MAJOR DIMENSIONSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 1 m3/hMARPOL IMO MEPC 107(49)6543224-0010-01 -01 1

654321DOIL CONTENT ALARM 15PPMDFILTER TANKSELECTRICAL CONTROL CABINET INSTRUMENT AIR DN 6mm OIL REMOVAL TANK CCA: OILY WATER INLET FROM BILGE MALE THREAD DN 25 B: OIL RELEASE OUTLET,TO SLUDGE TANK MALE THREAD DN 25 C: OPTIONAL WATER OUTLET TO JOWA EBU, FURTHER PROCESSED TO ACHIEVE &lt;5PPM MALE THREAD DN 25 D: WATER INLET FOR BACKFLUSH MALE THREAD DN25 E: WATER OUTLET, &lt;15 PPM FOR OVERBOARD DICHARGE MALE THREAD DN 25 F: BACKFLUSH WATER, RECIRCULATED WATER &gt;15 PPM AND DRAIN OUTLET TO BILGE TANK MALE THREAD DN 25BTANK T1 ANhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ODEBFILE NAME24-0010-01-01 3Sep 1m3.iam A3 Greg Shannon DRAWN 2004-09-17CHECKSIZEMODEL ID24-0010-01SCALE1:10AFILTER TANK ANODESAPPR. REVISO GA, CONNECTION POINTSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 1m3/hMARPOL IMO MEPC 107(49)6543224-0010-01 -02 1

695412321DEFFLUENT SAMPLE POINT 13 GRAVITY SEPARATOR TANK OIL RELEASE SAMPLE POINT 8 7 64D5 NOTES: 1. INTERNAL PIPE SPEC: 28 x 1.2 MTRL: COPPER 2. INTERNAL PLUMBING CONNECTIONS IN BRASS AND COPPER PRESS FITTING SYSTEM WITH OIL RESISTANT SEALS 3. ALL TANKS ANODE PROTECTED 4. SKID FRAME CONSTRUCTED IN S235 STEEL 5. FILTER MATERIAL JOWA F-200, 50kg TOTAL (2x25kg) 17 16 15 14 13 12 11 10 9 8 7 6 5 1 2 2 2 1 1 1 1 1 6 8 1 5 Safety V. Durgo 6 Bar DN20 F75 Strainer 0,5mm L=210mm F75 Strainer 1,0mm L=210mm 3Sep Drain Strainer 0,5mm L=85mm Oil Sensor CLM-36N JOWA-RTE 15ppm http://www.51wendang.com/doc/ecdebe501974f24dedd356c7Oil Alarm Pressure gauge, 0-10 Bar PRESSURE GAUGE VALVE CONTROL CABINET 3SEP BALL VALVE DN15 BALL VALVE DN25 3-Way Ball valve DN25 Pneumatic solenoid valve DN25 Normally Closed Non-Return Valve DN25 Filter Tank 75l GRAVITY SEP TANK 75l 3Sep Frame 1,0m3/h DESCRIPTIONSIZE7C5 10 15 3 4 7 1155BRASS Plastic Plastic Plastic0,480 kg 0,107 kg 0,107 kg 0,069 kg 1,078 kg 3,782 kg 0,100 kg 0,062 kg 30,770 kg 0,182 kg 0,735 kg 0,860 kg 1,500 kg 0,463 kg 25,384 kg 34,50 kg 91,224 kg MASS22303-20226 50100 - 21002 50075 - 22002 50075 - 21002 22311-03600 87081-00000 10109-00002 10107-08436 24001-00201 19001-15156 19054-25256 19059-25256 22304-00256 95030-00006 50075-50101 24-0010-01 24-0010-01 ID NUMBERSCALEC5 8 5 7 7BRASS BRASS BRASS BRASS BRASS BRASS brass AISI 316 AISI 316 S235 MTRLMODEL IDB 142 4 3 CUT AWAY VIEWS 8BFILTER TANKS OIL RELEASE SAMPLE POINT4 2 3 2 2 1 1 1 ITE QTFILE NAME24-0010-01-01 3Sep 1m3.iam Ahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c73 Greg Shannon DRAWN 2004-09-17CHECK24-0010-011:10A17 7 7 7 1671APPR. REVISO GA, PARTS LISTTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 1m3/hMARPOL IMO MEPC 107(49)6543224-0010-01 -03 1

654321DD1834675C8051780C545 415 28515518 1137 1045515BB1280 1523FILE NAME 24-0025-01-01 3Sep 2,5m3.iam DRAWN2004-07-06A3 Greg ShannonSIZEMODEL ID24-0025-01SCALE1:15A DRY MASS: 400,25 kg WORKING PRESSURE: 2 BAR MAINTENANCE AREA: 500mm PERIMETER IN FRONT OF UNITCOMPLIES WITH MARPOL IMO MEPC 107(49)CHECK APPR. REVGA, MAJOR DIMENSIONSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 2,5m3/hMARPOL IMO MEPC 107(49)6543224-0025-01 -01 1

654ELECTRICAL CONTROL CABINET321DINSTRUMENT AIR DN 6mmDFILTER TANKSOIL REMOVAL TANKA: Ohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ILY WATER INLET C FROM BIILGE MALE THREAD DN 25 B: OIL RELEASE OUTLET,TO SLUDGE TANK MALE THREAD DN 25 C: OPTIONAL WATER OUTLET TO JOWA EBU, FURTHER PROCESSED TO ACHIEVE &lt;5PPM MALE THREAD DN 25 D: WATER INLET, B FOR SYSTEM BACKFLUSH MALE THREAD DN 25 E: WATER OUTLET, &lt;15 PPM FOR OVERBOARD DICHARGE MALE THREAD DN 25 OIL CONTENT ALARM 15PPM TANK T1 ANODEFILE NAME 24-0025-01-01 3Sep 2,5m3.iam DRAWN CHECK SIZE MODEL ID SCALECB2004-07-06A3 Greg Shannon24-0025-011:10A F: BACKFLUSH WATER, RECIRCULATED WATER &gt;15 PPM AND DRAIN OUTLET TO BILGE TANK MALE THREAD DN 25 6 5 4APPR.FILTER TANK ANODESREVISO GA, CONNECTION POINTSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 2,5m3/hMARPOL IMO MEPC 107(49)3224-0025-01 -02 1

6851343 11321DNOTES: 1. INTERNAL PIPE SPEC: 28 x 1.2 MTRL: COPPER 2. INTERNAL PLUMBING CONNECTIONS IN BRASS AND COPPER http://www.51wendang.com/doc/ecdebe501974f24dedd356c7PRESS FITTING SYSTEM WITH OIL RESISTANT SEALS 3. ALL TANKS ANODE PROTECTED 4. SKID FRAME CONSTRUCTED IN S235 STEEL 5. FILTER MATERIAL JOWA F-200, 100kg TOTAL (4x25kg SACKS)DEFFLUENT SAMPLE POINT4GRAVITY SEPARATOR TANK OIL RELEASE SAMPLE POINT 4 7C7 6 9 10 12 7 5 1417 16 15 14 13 12 11 10 9 8 7127 74 4 12B3 2 4 4 17 CUT AWAY VIEWS 3 FILTER TANKS OIL RELEASE SAMPLE POINT6 5 4 3 2 1 ITEDRAWN CHECK1 Safety V. Durgo 6 Bar DN20 2 3Sep Drain Strainer 0,5mm L=85mm 2 F150 Strainer 0,5mm 2 F150 Strainer 1,0mm.ipt 1 JOWA-RTE 15ppm Oil Alarm 3 BALL VALVE DN15 1 Oil Sensor CLM-36N 1 PRESSURE GAUGE VALVE DN8 1 Pressure gauge, 0-10 Bar 1 CONTROL CABINET 400X370X210 5 Pneumatic solenoid valve DN25 NC 1 3-Way Ball valve DN25 2 Non-Return Valve DN25 8 BALL VALVE DN25 2 FILTER TANK 150 L 1 3Sep Gravity Tank 2,5m3h 1 3Sep frame 2,5m3 QT DESCRIPTION2004-07-06BRASS Plastic Plastic Plastic BRASS Brass Brass0,480 kg 0,069 kg http://www.51wendang.com/doc/ecdebe501974f24dedd356c72,247 kg 2,247 kg 3,782 kg 0,182 kg 1,078 kg 0,062 kg 0,100 kg 30,770 kg 1,500 kg 0,860 kg 0,463 kg 0,735 kg 56,926 kg 76 kg 118,74 kg MASS22303-20226 50075 - 21002 50150 - 22002 50150 - 21002 87081-00000 19001-15156 22311-03600 10107-08436 10109-00152 24001-00201 22304-00256 19059-25256 95030-00006 19054-25256 50150-00101 24-0025-01 24-0025-01 ID NUMBERSCALECBRASS BRASS brass BRASS AISI316L AISI316L S235 MTRLMODEL IDBFILE NAME 24-0025-01-01 3Sep 2,5m3.iamA3 Greg ShannonSIZE24-0025-011:15A4 15 16 4 1APPR. REVISO GA, PARTS LISTTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 2,5m3/hMARPOL IMO MEPC 107(49)6543224-0025-01 -03 1

654321DD1834 954 794 634C4741780C25 622 1210117031413761541450 1530 1807FILE NAME4080395B475n14(x4)8080B24-0050-01-01 3Sep 5m3.iam A3 Greg Shannon DRAWN 2004-06-30http://www.51wendang.com/doc/ecdebe501974f24dedd356c7SIZEMODEL ID24-0050-01SCALE1:20ADRY MASS: 511,83kg WORKING PRESSURE: 2 BAR MAINTENANCE AREA: 500mm PERIMETER IN FRONT OF UNIT COMPLIES WITH MARPOL IMO MEPC 107(49)CHECK APPR. REV#1 041214 GS GA, MAJOR DIMENSIONSID NOTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40JOWA ABAJOWA 3SEP OWS 5 m3/hMARPOL IMO MEPC 107(49)6543224-0050-01 -01 1

65432ELECTRICAL CONTROL CABINET1FILTER TANKSDINSTRUMENT AIR DN 6 OIL CONTENT ALARM 15PPMDOIL REMOVAL TANKCA: OILY WATER INLET FROM BIILGE MALE THREAD DN 40 B: OIL RELEASE OUTLET, TO SLUDGE TANK MALE THREAD DN 40 C: OPTIONAL WATER OUTLET TO JOWA EBU, FURTHERPROCESSED TO ACHIEVE &lt;5PPM MALE THREAD DN 40 D: WATER INLET, FOR SYSTEM B BACKFLUSH MALE THREAD DN 25 E: WATER OUTLET, &lt;15 PPM FOR OVERBOARD DICHARGE MALE THREAD DN 40 F: BACKFLUSH WATER, RECIRCULATED WATER &gt;15 PPM AND DRAIN OUTLET TO BILGE TANK MALE THREAD http://www.51wendang.com/doc/ecdebe501974f24dedd356c7DN 40CBFILTER TANK ANODESTANK T1 ANODESFILE NAME24-0050-01-01 3Sep 5m3.iam A3 Greg Shannon DRAWN 2004-06-30CHECK APPR. REVSIZEMODEL ID24-0050-01SCALE1:15A#1 041214 GS ISO GA, CONNECTION POINTSID NOTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40JOWA ABAJOWA 3SEP OWS 5 m3/hMARPOL IMO MEPC 107(49)6543224-0050-01 -02 1

6514 7 248 5 43219DEFFLUENT SAMPLE POINT GRAVITY SEPARATOR TANK OIL RELEASE SAMPLE POINTNOTES: 1. INTERNAL PIPE SPEC: 40 x 1.2 MTRL: COPPER 2. INTERNAL PLUMBING CONNECTIONS IN BRASS AND COPPER PRESS FITTING SYSTEM WITH OIL RESISTANT SEALS 3. ALL TANKS ANODE PROTECTED 4. SKID FRAME CONSTRUCTED IN S235 STEEL 5. FILTER MATERIAL JOWA F-200, 200kg TOTAL (8x25kg)D4 5C13 5 10 7 15 11 518 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 ITE512 3B3 2 126FILTER TANKS OIL RELEASE SAMPLE POINT CUT AWAY VIEWS1 Safety V. Durgo 6 Bar http://www.51wendang.com/doc/ecdebe501974f24dedd356c7DN20 2 3Sep Drain Strainer 0,5mm L=85mm 2 F150 Strainer 0,5mm 2 F150 Strainer 1,0mm.ipt 1 JOWA-RTE 15ppm Oil Alarm 1 3-Way Ball valve DN25 5 BALL VALVE DN25 1 Pressure gauge, 0-10 Bar 1 PRESSURE GAUGE VALVE DN8 1 CONTROL CABINET 400X370X210 1 Oil Sensor CLM-36N 3 BALL VALVE DN15 2 NON RETURN VALVE DN32 5 PNEUMATIC VALVE N.C. DN32 3 BALL VALVE DN32 2 FILTER TANK 300 L 1 3Sep Gravity Tank 1 3Sep frame 5m3 QT DESCRIPTIONSIZEBRASS Plastic Plastic Plastic BRASS BRASS Brass BRASS0,480 kg 0,069 kg 2,247 kg 2,247 kg 3,782 kg 0,860 kg 0,735 kg 0,100 kg 0,062 kg 30,770 kg 1,078 kg 0,182 kg 1,230 kg 2,796 kg 0,800 kg 80,845 kg 110 kg 128,311 kg MASS22303-20226 50075 - 21002 50150 - 22002 50150 - 21002 87081-00000 19059-25256 19054-25256 10109-00152 10107-08436 24001-00201 22311-03600 19001-15156 95030-32006 22304-00326 19001-32326 50300-00101 24-0050-01 24-0050-01 ID NUMBER1:20CBRASS BRASS BRASS BRASS AISI316L AISI316L S235 MTRLMODhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7EL IDBFILE NAME24-0050-01-01 3Sep 5m3.iam A3 Greg Shannon DRAWN 2004-06-30CHECK APPR. REV24-0050-01SCALE18A12 112 4 16 17 12#1 041214 GS ISO GA, PARTS LISTID NOTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40JOWA ABAJOWA 3SEP OWS 5m3/hMARPOL IMO MEPC 107(49)6543224-0050-01 -03 1

654321DD2184 955 795 635C4751780C315 15533 15107621685BB1880 2238FILE NAME SIZE MODEL ID SCALE24-0100-01-01 3Sep 10m3.iamADRY MASS: 853,60 kg WORKING PRESSURE: 2 BAR MAINTENANCE AREA: 500mm PERIMETER IN FRONT OF UNIT COMPLIES WITH MARPOL IMO MEPC 107(49)DRAWN CHECK APPR. REV2004-07-12A3 Greg Shannon24-0100-011:25GA, MAJOR DIMENSIONSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 10m3/hMARPOL IMO MEPC 107(49)6543224-0100-01 -01 1

654321DELECTRICAL CONTROL CABINhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ET INSTRUMENT AIR DN 6FILTER TANKSDOIL REMOVAL TANKCA: OILY WATER INLET FROM BIILGE MALE THREAD DN 40 B: OIL RELEASE OUTLET, TO SLUDGE TANK MALE THREAD DN 40 C: OPTIONAL WATER OUTLET TO JOWA EBU, FURTHERPROCESSED TO ACHIEVE &lt;5PPM MALE THREAD DN 40CBBOIL CONTENT ALARM 15PPM D: WATER INLET, FOR SYSTEM BACKFLUSH MALE THREAD DN 25 E: WATER OUTLET, &lt;15 PPM FOR OVERBOARD DICHARGE MALE THREAD DN 40 FILTER TANKS TANK T1 ANODEFILE NAME DRAWN CHECK APPR. REV24-0100-01-01 3Sep 10m3.iam2004-07-12A3 Greg ShannonSIZEMODEL ID24-0100-01SCALE1:15AF: BACKFLUSH WATER, RECIRCULATED WATER &gt;15 PPM AND DRAIN OUTLET TO BILGE TANK MALE THREAD DN 40ISO GA, CONNECTION POINTSTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABAJOWA 3SEP OWS 10m3/hMARPOL IMO MEPC 107(49)6543224-0100-01 -02 1

6512 13 12 1048321D4NOTES: 1. INTERNAL PIPE SPEC: 42 xhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 1.6 MTRL: COPPER 2. INTERNAL PLUMBING CONNECTIONS IN BRASS AND COPPER PRESS FITTING SYSTEM WITH OIL RESISTANT SEALS 3. ALL TANKS ANODE PROTECTED 4. SKID FRAME CONSTRUCTED IN S235 STEEL 5. FILTER MATERIAL JOWA F-200, 500kg TOTAL (20x25kg)DGRAVITY SEPARATOR TANK OIL RELEASE SAMPLE POINT 87 8 9 12 5 8 3 EFFLUENT SAMPLE POINTC17 16 15 14 13 12 11 10 9 81 2 2 2 1 3 1 1 1 58 1281115B7 26 3FILTER TANKS OIL RELEASE SAMPLE POINT7 6 5 43 2 5 1CUT AWAY VIEWS 173 2 2 1 1 1 ITE QTFILE NAME DRAWNSafety V. Durgo 6 Bar DN20 F150 Strainer 0,5mm F150 Strainer 1,0mm.ipt 3Sep Drain Strainer 0,5mm L=85mm JOWA-RTE 15ppm Oil Alarm BALL VALVE DN15 Brass Pressure gauge, 0-10 Bar Oil Sensor CLM-36N 3-Way Ball valve DN25 PNEUMATIC SOLENOID VALVE OBLIQUE SETTING DN40 NC BALL VALVE DN40 NON RETURN VALVE DN40 BALL VALVE DN25 CONTROL CABINET 400X370X210 FILTER TANK 750L 3Sep Gravity Tank 10m3h 3Sep frame 10m3 DESCRIPTIONA3 Ghttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7reg ShannonSIZEBRASS Plastic Plastic Plastic0,480 kg 2,247 kg 2,247 kg 0,069 kg 3,782 kg 0,182 kg 0,100 kg 1,078 kg 0,860 kg 3,166 kg22303-20226 50150 - 22002 50150 - 21002 50075 - 21002 87081-00000 19001-15156 10109-00002 22311-03600 19059-25256 22304-00406CBRASS Brass BRASS BRASSBrass BRASS BRASS3,515 kg 2,899 kg 0,735 kg 30,770 kg19001-40406 95030-42006 19054-25256 24001-00201BAISI316L 176,290 kg 50750-00101 24-0100-01 AISI316L 204 kg S235 147,20 kg 24-0100-01 MTRL MASS ID NUMBERMODEL ID24-0100-01-01 3Sep 10m3.iam24-0100-01SCALE1:202004-07-12A51 5 7 5 14 5CHECK APPR. REVISO GA, PARTS LISTTULEBO 865 G&#246;teborg-SWEDEN Teleph.  46 31 795 00 40ID NOJOWA ABA16JOWA 3SEP OWS 10m3/hMARPOL IMO MEPC 107(49)6543224-0100-01 -03 1

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard10.0 Electrical Drawings and Pneumatic DrawingsK:1-Nhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7YA K1-JOWA PRODUKTER3SEP32/41

D

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard11.0 Oil Content Meter Operating ManualK:1-NYA K1-JOWA PRODUKTER3SEP33/41

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard11.1Rivertrace AlarmK:1-NYA K1-JOWA PRODUKTER3SEP34/41

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04RIVERTRACE ENGINEERING LTD109080 INSTRUCTION MANUAL BILGE OIL ALARMUNIT P, KINGSFIELD BUSINESS CENTRE PHILANTHROPIC ROAD REDHILL, SURREY, RH1 4DPTELEPHONE:  44(0)870 770 2721 FAX:  44(0)870 770 2722 WEB: http://www.51wendang.com EMAIL: service@http://www.51wendang.com

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 1Introduction1.1 1.2 1.http://www.51wendang.com/doc/ecdebe501974f24dedd356c73 Important Notes SMART CELL - BILGE Overview Specification Listing 2 2 3Section 2Installation2.1 2.2 2.3 2.4 Construction details Mounting Pipe work and Connections Electrical Connections 5 6 7 8Section 3Commissioning3.1 3.2 3.3 Piping Electrical Functional testing 11 11 11Section 4Operating Instructions4.1 4.2 4.3 4.4 4.5 4.6 4.7 Getting Started Clean Water Calibration Set Alarm Points Set Alarm Delays Set Analogue out View IMO Data Diagnostics 12 14 15 16 17 17 18Section 5Maintenance and Spares5.1 5.2 5.3 Maintenance (weekly) Maintenance (Yearly) Spares 20 20 20Section 6Trouble Shooting &amp; Contact6.1 6.2 Trouble Shooting Guide Tech Support registration 21 22RIVERTRACE ENGINEERING LIMITEDPage 1 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 1 Introduction1.1 Important Notes &#167; &#167; &#167; &#167; &#167; &#167; &#167; &#167; &#167;All National or locahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7l codes of practice or regulations must be observed and, where applicable, are deemed to take precedence over any directive or information contained in this manual. This equipment must be installed and operated in strict accordance with the instructions contained in this manual. Failure to do so will impair the protection provided. Installation and retro fitting of parts listed in section 4.4 must be undertaken by a competent and suitably skilled person. Servicing, other than replacement of spares, must be undertaken by an RTE approved service centre. The equipment must be provided with a sound electrical earth connection. The unit must be isolated from the electrical supply before any maintenance of the equipment is attempted. Hazardous voltages are present within the monitor enclosure and solenoid valve assembly. It is essential that maintenance is carried out as described in section 5. Failure to do this will impair the functionalhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ity of the equipment and could lead to permanent damage to the monitor. The SMART CELL enclosure must not be opened. If opened a cell breach error will be displayed on the screen (this error can not be reset) and the “VOID” tamper proof labels on either side of the enclosure lid will be destroyed.1.2SMART CELL - BILGE OverviewThe SMART CELL - BILGE Monitor has been designed specifically for use in conjunction with 15ppm oily-water separator units. It has a specification and performance which meets the requirements of the International Maritime Organisation specifications for Bilge Alarm Units contained in Resolution MEPC 107 (49). Analysis of the oily water sample is undertaken by a unique detector array arrangement. A narrow beam of light is emitted across a glass cell tube which the oily water sample passes through. Light scattered and transmitted is detected across the array and passed through a complex oil content calculatiohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7n algorithm. The resulting oil content is then displayed on the LCD screen. Two oil alarm relays and a 0-20mA / 4-20mA output are provided to control the overboard discharge and to view / record oil content levels remotely.RIVERTRACE ENGINEERING LIMITEDPage 2 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04To meet the new requirements of MEPC 107(49) an on board flash memory, Real time clock, dual switch input and clean water / sample selection valve are fitted. These are described in more detail in the operating instructions (section 4).1.3Specification ListingMeasurementOil types: Clean water calibration: Oil range: Resolution: Accuracy oil   solids : Solids discrimination: Response time: Fuel Oil, Diesel and Mixture C (IMO defined)  /- 2ppm of factory set values 0 - 30 ppm (trend to 40) all types 0.1 ppm  /- 5ppm up to 30 ppm 10, 50 and 100ppm Iron Oxide at 10 ppm Diesel &lt; 5 sec http://www.51wendang.com/doc/ecdebe501974f24dedd356c7(oil reading)AlarmsOil alarm 1 setpoint: Oil alarm 2 setpoint: Oil alarm 1 delay: Oil alarm 2 delay: Alarm hysterisis: Alarm contacts: 1 – 15 ppm user adjustable 1 - 15 ppm user adjustable 0 – 5 seconds user adjustable 0 – 600 seconds user adjustable in 10 sec increments 0.5 ppm 2 SP Alarm Relays 10A @ 250VAC (NC in alarm)User InterfaceLCD display: Control: 4 x 16 alphanumeric back lit LCD display 3 button keypadInput / OutputAnalogue output: Communications: Cable terminals: Cable glands: Switch inputs: Loop powered 4-20mA / 0 - 20mA 24V RS232 - output Accept cores of 2.5mm&#178; (HV) and 1.5mm&#178; (LV) 4 x spare, to accept cable diameters 10 – 12mm dia. 2 x switch inputs for separator &amp; flow statusData Storage and RetrievalCalibration data storage: IMO required data: Stored onboard microcontroller in Smart Cell Stored in Control enclose (SMART CELL may be changed with data remaining on board) IMO required data retrhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ieval: Via LCD display or RS 232 communication linkRIVERTRACE ENGINEERING LIMITEDPage 3 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Environmental &amp; SampleAmbient humidity: Ambient temperature: Sample / clean water temperature1: Sample / clean water flow rate: Sample / clean water pressure: Sample / clean water select: Sample pipe fittings: Inclination 90%RH Max @ 55&#176;C 0&#176;C -  60&#176;C  1&#176;C -  60&#176;C 0.5 - 4.0 litres / min 0.1 bar - 10 bar 3 way universal solenoid valve &#188; inch BSPP 25&#176; in any plane from normal mountingSystem and SupplySupply voltage: Supply voltage Consumption: Supply voltage tolerance: Other supply tolerance: Projected life: Protection class: Approvals: 115 or 230V AC, 50 – 60Hz (24VAC available) &lt; 50 VA including solenoid valve  /- 15%  /- 10% &gt; 50,000 hrs IP 65 EU MED (GL)   USCG to IMO MEPC 107(49)Construction and other Crihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7teria.Security: Protection of all calibration dependent items plus software lock Auto clean (optional) : Manual clean: Weight: User set 1 – 360 min (if fitted) Fitted as standard 3.2 KgRIVERTRACE ENGINEERING LIMITEDPage 4 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 2 Installation2.1 Construction DetailsThe SMART CELL - BILGE Monitor is split into two logical modules. The display / control module (2) (left) contains the membrane keypad, LCD display and the Smart Bilge Control PCB. Contained on this PCB are all the control and data storage associated electronics in addition to all the customer terminations which can be accessed via the cable glands(5). This PCB links a 5 volt supply and RS485 communications to the Cell electronics via a 4 wire interface cable. The SMART CELL (1), contains the optoelectronics and mechanics used in the calculation of the sample oil content. UNDERhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 NO CIRCUMSTANCE IS THIS ENCLOSURE TO BE OPENED. Sample (7) and clean water (8) lines are connected to the solenoid valve to allow automatic selection of clean water for clean water calibration and diagnostics. Sample/Clean water is exhausted from the monitor via the outlet (6) after passing through the measuring sensor. A manual cell clean unit (3) is provided which must be used in accordance with the maintenance requirements in section 5. The throttle (9) can be used to increase or decrease the back pressure in the cell. This is especially useful if air is present in the sample.Fig 2.1 Construction detailsFIXING HOLES FOR M6 TYPICAL 4 POSNS3 6 21SMART - MEASURING CELL SMART - DISPLAY/CONTROL MODULE MANUAL CLEAN 3 WAY SOLENOID VALVE (230,115,24 VAC VARIANTS) CABLE GLANDS IP68 RATED FOR CABLE &#216;10 - 14 SAMPLE OUPUT CONNECTION CUSTOMER FITTING 1/4&quot; BSPP REQD SAMPLE INPUT CONNECTION CUSTOMER FITTING 1/4&quot; BSPP REQDhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 CLEAN WATER INPUT CONNECTION CUSTOMER FITTING 1/4&quot; BSPP REQD THROTTLE3WARNING - HAZARDOUS VOLTAGE INSIDE!DO NOT OPEN NO SERVICEABLE PARTS INSIDE!THROTTLE ADJ9WARNING RTE CALIBRATION VOID4SMART - BILGERTE WARNING RTE CALIBRATION VOID52SMART - CELL205.0RTERIVERTRACE ENGINEERINGRTERIVERTRACE ENGINEERING235.01RTE28967895 4 7 8WEIGHT:- 3.2 Kg275.0295.0RIVERTRACE ENGINEERING LIMITED148.5Page 5 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.042.2Mounting DetailsThe SMART CELL - BILGE monitor should be located on or in close proximity to the oily-water separator to minimise response delays. Under no circumstances should the distance between the monitor and the separator exceed a distance that would result in a response time of more than 20 seconds and breaching IMO regulations.MountingMount the SMART CELL - BILGE by means of 4http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 x M6 bolts on to a rigid vertical surface and preferably with the display panel of the monitor at operator eye level.Fig 2.2 Mounting DetailsFIXING HOLES FOR M6 TYPICAL 4 POSNSWARNING - HAZARDOUS VOLTAGE INSIDE!DO NOT OPEN NO SERVICEABLE PARTS INSIDE!THROTTLE ADJSMART - CELL205.0RTERIVERTRACE ENGINEERINGRTERIVERTRACE ENGINEERING275.0RIVERTRACE ENGINEERING LIMITEDPage 6 of 22RTEWARNING RTE CALIBRATION VOIDSMART - BILGERTE WARNING RTE CALIBRATION VOID

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.042.3Pipe Work and ConnectionsFig 2.3 Shows all pipe fittings required for Sample In, Clean Water In and Sample Out. All fittings must be BSPP.Fig 2.3 Pipe FittingsANTI SIPHON TUBE 2 Metre Minimium3SAMPLE OUT 10mm PIPING200mm MinWARNING - HAZARDOUS VOLTAGE INSIDE!DO NOT OPEN NO SERVICEABLE PARTS INSIDE!THROTTLE ADJSMART - BILGESMART - CELLRThttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ERIVERTRACE ENGINEERINGRTERIVERTRACE ENGINEERINGSAMPLE IN1CLEAN WATER IN2DRAIN ENSURE LEVEL IS CLEAR OF BILGE WATERItem No. 1 2 3Description Sample Inlet 1/4 inch BSPP fitting Clean Water Inlet 1/4 inch BSPP fitting Sample Outlet 1/4 inch BSPP fittingRIVERTRACE ENGINEERING LIMITEDPage 7 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.042.4Electrical ConnectionsWARNING: Hazardous voltages are present In the control enclosure – Ensure equipment is isolated before proceeding.Please read the following points before attempting any electrical work.&#167; &#167; &#167; &#167;Ensure all cabling is volt free and isolated. This unit must be connected to the mains supply via a suitably rated double pole (3mm contact gap), 1 amp fused, isolator unless such fusing/isolation is provided by associated equipment. Isolator should be clearly marked as to function. Cable gland entrieshttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 can accept cables from 10 to 12 mm diameter and terminal blocks will accept cable cores of 2.5mm&#170; (mains / Alarm contacts ) and 1.5 mm&#170; ( terminals less than 48 V ) . Cables carrying hazardous voltages must be at least 0.5 mm&#170; csa. When terminating mains cabling at monitor and electrical source, the earth conductor must be made longer than the live and neutral conductors.User terminations are located by removing the lid from the SMART Display/Control module via the four screws. A protection plate is situated above the terminals which must be removed via 4 M3 screws.Fig 2.4.1 User TerminationsRTE CONNECTION TO DISPLAY INTERNAL 1 J13 RTE RTE CONNECTION TO CONNECTION TO MEMBRANE SMART CELL INTERNAL INTERNAL 1J14 KEYPAD 1 J15 SMART-CELL 1 J12 JTAG Tx 1 J11 RS232 Rx 1 J9 SW1 1 J7 SW2 RS232 CONNECTION CUSTOMER VOLT FREE SWITCH INPUTS - SEPARATOR ON/OFF STATUS CUSTOMER VOLT FREE SWITCH INPUTS - BACKFLUSH/OTHER0-20mA 4http://www.51wendang.com/doc/ecdebe501974f24dedd356c7-20mA ANALOGUE OUTPUTJ8 4-20mA   1 1J6IO PORTJP1 TO BE LINKED IF 24VAC IS REQUIRED FUSE F1 250V 1.25A ANTI SURGEJP1LJ1 E ~NLJ2 E NLJ3 EN 1J4 2 31J5 23SUPPLY INAUTO-CLEAN SAMPLE-CLEAN ALARM 1 ALARM 2RIVERTRACE ENGINEERING LTD. SMARTBILGE PCBCUSTOMER INPUT 230-110 VAC OR 24VAC 50 - 60 Hz OUTPUT FOR OPTIONAL AUTO CLEAN FACILITY RTE CONNECTIONOUTPUT TO SOLENOID VALVE RTE CONNECTION NORMALLY CLOSED IN ALARM MODE OUTPUTS FOR CUSTOMERRIVERTRACE ENGINEERING LIMITEDPage 8 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Table 2.4.2 User Terminal instructionTerminal J1 - L J1 - E J1 - N J2 - L J2 - E J2 - N J3 - L J3 - E J3 - N J4 - 1 J4 - 2 J4 - 3 J5 - 1 J5 - 2 J5 - 3 J7 - 1 J7 - 2 J8 - 1 J8 - 2 J9 - 1 J9 - 2 J11 - 1 J11 - 2 J11 - 3Terminal description Live in 24/115/230 V AC Earth Neutral in 24/115/230 V AC Live 24/115/230 V AC Earth Neutral 24/115/230http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 V AC Live 24/115/230 V AC Earth Neutral 24/115/230 V AC Normally closed contact contact Normally open contact Normally closed contact contact Normally open contact 5V DC Switch In  24V DC 0V 5V DC Switch In Tx GND RxTerminal block description Customer Supply Mains input from suitable rated IsolatorMax ratings250V AC, 40 VA max.Auto clean control. Note: wiring (if present) to this terminal is not to be altered. Sample clean control. Note: wiring to this terminal is not to be altered. Alarm 1 relay contacts, normally closed in power down and alarm active states. Alarm 2 relay contacts, normally closed in power down and alarm active states.250V AC , 500mA.250V AC, 500mA.250V AC/DC, 10A.250V AC/DC, 10A.Customer Switch Input 1 4-20mA Connection 0-20mA Connection Customer Switch Input 25V DC 20mA24V DC 20mA5V DC 20mARS232 Connection /-12V DC 10mARIVERTRACE ENGINEERING LIMITEDPage 9 of 22

SMART http://www.51wendang.com/doc/ecdebe501974f24dedd356c7CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Precise wiring details will vary dependant upon the control system to be employed but the most frequently used systems employ Alarm relay 1 for control purposes, which must be used to control the overboard discharge valve and Alarm relay 2 for alarm annunciation only. Typical Control System Re-circulate on Alarm A recirculation system employs Alarm relay 1 to control a solenoid valve which energises or de-energises a pneumatically operated 3 way valve.RIVERTRACE ENGINEERING LIMITEDPage 10 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 3 Commissioning3.1 Piping &#167; &#167; 3.2Check all piping for leaks and rectify where appropriate Ensure all piping and fittings conform to specifications set in section 2.3.Electrical &#167; &#167; &#167;Check that correctly rated isolator is connected to the mains input (see sectiohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7n 2.4.). Check the SMART CELL - BILGE is correctly earthed. Check all cabling conforms to specifications set out in Table 2.4.3.3Functional testing &#167; &#167;Follow section 4 to start up and run clean water calibration. Follow section 6 for trouble shooting should any errors/spurious readings result.RIVERTRACE ENGINEERING LIMITEDPage 11 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 4 Operating instructions4.1 Getting StartedThe SMART CELL - BILGE is controlled and set up by the user interface on the Display/Control Module. Use the diagram in Fig 4.1.1 to become familiar with the controls,Fig 4.1.1 User interface4 x 16 Alphanumeric LCD DisplayRed user interface Keys ENTER, UP and DOWNRIVERTRACE ENGINEERING LIMITEDPage 12 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04On power up the user will be presented with a screen as http://www.51wendang.com/doc/ecdebe501974f24dedd356c7shown in Fig 4.1.2.&#167; &#167; &#167; &#167;At the top of the display the user will see the oil concentration in Parts Per Million (PPM). The status of the two oil alarms will be displayed. The date and time is displayed. (time is set to GMT / UTC ). If either of the alarm set points is passed the LCD backlight will flash.Fig 4.1.2 Screen Shot - Main Information ScreenShows Oil Concentration in PPMAlarm 1 state Alarm 2 stateDate &amp; Time DisplayTo interrogate the SMART CELL - BILGE Monitor settings the user can press any of the Interface Keys to bring up the Menu Options Screen as shown in Fig 4.1.3Fig 4.1.3 Screen Shot - Menu Screen OptionsUse the DOWN and UP Keys to view all the Menu options. Press ENTER on any option to select or on Escape to return to main information screen.RIVERTRACE ENGINEERING LIMITEDPage 13 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.044.2Clhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ean Water CalibrationA clean water calibration can be performed to account for differences in clean water between the factory calibrated clean water and the ships own clean water supply. On activation of the clean water calibration the clean water / sample solenoid will select clean water. The SMART CELL - BILGE will then average the clean water reading over the period of 30 seconds after which a further 10 seconds will lapse for the user to verify the calibration in monitor mode before the solenoid selects sample once more. To set the clean water calibration enter the Menu screen as shown in Fig. 4.1.3 and scroll down until the cursor reaches &quot;Clean wtr cal&quot; then press the ENTER key. The screen will change as shown in Fig 4.2.2.Fig 4.2.2 Screen Shot - Menu Screen OptionsThe screen will display for 30 seconds after which, it will return to that shown in Fig 4.1.3. The solenoid will select clean water for a further 10 sehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7conds so that the clean water reading can be verified.RIVERTRACE ENGINEERING LIMITEDPage 14 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.044.3Set Alarm PointsThe SMART CELL - BILGE Monitor has two independent oil alarm contacts for user termination. These can be set by the user to operate when the displayed Oil content reaches the required Parts per Million (PPM) settings. Note: The alarms have a 0.5 hysteresis included to prevent relay chatter. E.g if an alarm is set at 15 ppm and the oil concentration exceeds 15 ppm, the alarm will be activated. The alarm will not deactivate until the oil concentration drops below 14.5 ppm. To set the required Alarm points enter the Menu screen as shown in Fig. 4.1.3 and scroll down until the cursor reaches &quot;Set alrm point&quot; then press the ENTER key. The screen will change as shown in Fig 4.3.1.Fig 4.3.1 Screen Shot - Alarm Set OptionsMovehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 the cursor to Alarm 1 set by pressing the DOWN key and then press ENTER. This will bring up the screen as shown in Fig 4.3.2. Note: Alarm 1 only must be used for control of the overboard discharge valve.Fig 4.3.2 Screen Shot - Alarm PPM ValueThe PPM value can now be set. The range is between 1 &amp; 15. Use the UP or DOWN key to select the required value. Once the required value has been selected press the ENTER key. This will bring the screen back to Fig 4.3.1. Repeat this operation to set the value for alarm 2. Press the ENTER key 3 times to return to the main information screen as shown in Fig 4.1.2.RIVERTRACE ENGINEERING LIMITEDPage 15 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.044.4Set Alarm DelaysOnce the alarm points have been set as described in Section 4.3, the alarm delay values can be entered. The alarm delay can be used so that if the oil concentration rises above the http://www.51wendang.com/doc/ecdebe501974f24dedd356c7oil alarm set point for a period exceeding the alarm delay value the alarm relay will activate and only de-activate once the Oil Concentration has fallen below the Alarm Set Point. Note: The main information display screen will show if an oil alarm is less or more than the current oil reading regardless of the alarm delay. To set the required alarm delays go the menu screen as shown in Fig. 4.1.3 and scroll down until the &quot;Set alrm delay&quot; then press the ENTER key. The screen will change as shown in Fig 4.4.1Fig 4.4.1 Screen Shot - Alarm Delay OptionsMove the cursor to delay 1 Set by pressing the DOWN key and then press ENTER. This will bring up the screen as shown in Fig 4.4.2.Fig 4.4.2 Screen Shot - Alarm Set Delay ValueAlarm delay 1 value can now be set between 0 &amp; 5 Seconds. Use the UP or DOWN key to select the required value. Once the required value has been selected press the ENTER key, this will bring the schttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7reen back to Fig 4.4.1. Repeat this operation to set the value for delay 2 (range between 0 &amp; 600 Seconds in 10 second increments). Press the ENTER key 3 times to return to the main information screen as shown in Fig 4.1.2.RIVERTRACE ENGINEERING LIMITEDPage 16 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.044.5Set Analogue OutThe analogue signal output can be set to either 0 – 20 mA or 4 - 20 mA and is scaled from 0 to 30 ppm calculated oil concentration. To set the required analogue signal output go to the menu screen as shown in Fig. 4.1.3 and scroll down until the &quot;Set analog out&quot; then press the ENTER key. The screen will change as shown in Fig 4.5.1.Fig 4.5.1 Screen Shot - Analogue Output OptionsMove the cursor using the UP or DOWN key to select required option. Press the ENTER key twice to return to the main information screen as shown in Fig 4.1.2.4.6View IMO Dhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ataIt is required that the date, time, bilge alarm status and separator status is to be recorded a for any change in alarm status or separator status and stored for a minimum of 18 months. This data is recorded within the Smart Control / Display enclosure, allowing replacement of the SMART CELL - BILGE whilst ensuring the data remains on board. The separator status is recorded via the SW1 and SW2 inputs. recommended. SW1 SW2 Separator ON/OFF status. Other separator status The following configuration is(if required).Note. SW2 will select clean water and active alarms permanently when closed The configuration of the switches must be recorded on board and date stamped. To view or download the IMO required data go to the Menu screen as shown in Fig. 4.1.3 and move the curser down until &quot;View IMO data&quot; then press the ENTER key. The screen will change as shown in Fig 4.6.1.Fig 4.6.1 Screen Shot - View IMO DataMove the curhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7sor to either View IMO data or Dump IMO data by pressing the DOWN key and then press ENTER. This will bring up a screen as shown in Fig 4.6.2 or Fig 4.6.3.RIVERTRACE ENGINEERING LIMITEDPage 17 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Fig 4.6.2 Screen Shot - IMO DataThis screen displays one IMO record at a time. Each record shows the oil content, Alarm status, switch input status and time/date of the record. The users can scroll through the records by pressing the UP and DOWN keys. When inspection is complete the ENTER key will exit the userFig 4.6.3 Screen Shot - Dump IMO DataBy selecting the dump IMO data command, the complete IMO required data history is copied and dumped to the RS232 port. This can be captured by purchasing a Smart Bilge download cable with instructions from Rivertrace Eng, see section 5.4. The download data screen will remain displayed until dump is complete.http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 NOTE: Dump IMO data command will NOT erase any data4.7DiagnosticsTo view the diagnostics go to the menu screen as shown in Fig. 4.1.3 and scroll down until the &quot;Diagnostics&quot; then press the ENTER key. The screen will change as shown in Fig 4.7.1Fig 4.7.1 Screen Shot - DiagnosticsMove the cursor to either View detectors or View disp PPM by pressing the DOWN key and then press ENTER. This will bring up a screen as shown in Fig 4.7.2 or Fig 4.7.3.RIVERTRACE ENGINEERING LIMITEDPage 18 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Fig 4.7.2 Screen Shot – View detectorsOnce in view detectors, the solenoid valve will select clean water and the screen will display the current signals present for clean water. Pressing the ENTER key will leave the diagnostics screen and set the valve back to sample.Fig 4.7.3 Screen Shot – View disp PPMOnce in view detectors, the solenoid valvehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 will select clean water and the screen will display the current calculated ppm for clean water. Pressing the ENTER key will leave the diagnostics screen and set the valve back to sample.RIVERTRACE ENGINEERING LIMITEDPage 19 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 5 Maintenance and Spares5.1 Weekly Maintenance&#167;At weekly intervals the SMART CELL - BILGE should be run through clean water calibration and the Manual clean must be plunged and released 10 times.5.2Yearly Maintenance&#167; &#167;At yearly intervals (or where necessary) the wiper ring on the manual clean assembly should be replaced. This can be ordered from RTE directly as part no. 109039. Every IOPP survey, Cell Should be verified/re-calibrated by an RTE approved service centre (contact RTE for an approved list) or a replacement calibrated cell can be requested from RTE (see below).5.4SparesWhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7hen ordering spares, it is important to supply details of the type of monitor, serial number of monitor, part number of each spare required, its description and any other relevant information. RECOMMENDED ON-BOARD SPARES Item Cell wiper ring Fuse 1.25A OTHER SPARES Item Smart Cell Smart Bilge PCB Assy (115   230) Smart Bilge PCB Assy (24V) Membrane overlay LCD display module Smart Bilge Download Cable Solenoid valve (230V) Solenoid valve (115V) Solenoid valve (24V) Qty 1 1 1 1 1 1 1 1 1 Part Number 109171 109019 109168 109030 109068 109165 109059 109060 109061 Qty 1 1 Part Number 109039 109167RIVERTRACE ENGINEERING LIMITEDPage 20 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Section 6 Trouble Shooting Guide6.1 Trouble Shooting GuideTable 6.1 Trouble shooting guideCorrective ActionCheck Isolator Check fuse (F1). See fig 2.4.1. Check all ribbon cable connectors are firmly inserted.Symhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ptomsMonitor is switched on and the LCD screen is blankPossible CausePower is Isolated Failure of mains fuse. Loose ribbon cable connection.LCD display Module is damaged. Monitor stays in alarm or reading is inaccurate. Or Display shows SYS ERROR, Detector 0 – 7 Is under / over range. Dirty measuring cell.Contact RTE for a replacement LCD module (Section 5.4) Clean cell and perform Clean water calibration. Section 5.1 Correct cause of contaminants and run clean water calibration.Excessive Contaminates present in sample e.g. rust bacteria, emulsified oils, detergents, discoloration of water. Sample flow blocked or restricted. Air bubbles are present in the Sample.Or Display shows SYS ERROR, Oil content Is under / over range.Remove blockage or restriction.Turn throttle clockwise until air is removed from sample (taking care not to exceed the maximum operating pressure. Remove Manual clean unit and clean with a detergenthttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7. Check Wiper ring on the end of the piston and replace if necessary. Remove Solenoid valve and clean thoroughly. If problems persist Contact RTE for a replacement Solenoid valve (Section 5.4).Manual Clean has become stuck in the down position.Sample / Clean water selection solenoid has a blockage.RIVERTRACE ENGINEERING LIMITEDPage 21 of 22

SMART CELL - BILGE - Instruction Manual Doc. 109080 Rev. A 10.08.04Display shows SYS ERROR, Temperature Is under / over range. Display shows SYS ERROR, Communications failure Current Ambient temperature inside the Cell is not within 0 - 60&#176; C. RS 485 communications cable is loose / not connected Cell Electronics Fault. Move equipment to an area with ambient temp between 0 - 60&#176; C. Ensure 4-pin plug is tightly inserted into J15. Fig 2.4.1Contact RTE for a replacement Cell (Section 5.4).Display shows SYS ERROR, RTC – I2C failureSmart Bilge electronics failure.http://www.51wendang.com/doc/ecdebe501974f24dedd356c7Contact RTE for a replacement Smart Bilge PCB (Section 5.4).Display shows SYS ERROR, Cell breach contact RTEMeasuring Cell has been opened.Contact RTE for a replacement measuring cell (Section 5.4).6.2Technical Support RegistrationTo receive automatic product updates, news and information, log on to http://www.51wendang.com and select tech support. Fill in the registration form and you will have access to support documents and the spares enquiry form.RIVERTRACE ENGINEERING LIMITEDPage 22 of 22

Date: Rev: Sign:2004-09-22 A GSJOWA 3SEP OWS OILY WATER SEPARATOR Standard11.2Deckma AlarmK:1-NYA K1-JOWA PRODUKTER3SEP35/41

INSTRUCTION MANUAL15ppm Bilge AlarmType OMD-2005DECKMA HAMBURG GmbHKieler Stra&#223;e 316, D-22525 Hamburg - Germany Tel.:  49 (0) 40 54 88 76-0, Fax:  49 (0) 40 54 88 76-10 Internet: http://www.51wendang.com eMail: post@http://www.51wendang.com

://www.51wendang.com/doc/ecdebe501974f24dedd356c7parDECKMA HAMBURG GmbHIMPORTANT NOTICEReplacement components for 15ppm Bilge Alarms.General All monitors in our range are inspected and tested to the related I.M.O. requirements at our factories prior to delivery. In normal use the units should operate correctly and without fault over a long period of time requiring only small amounts of maintenance to be carried out as outlined in the instruction manuals.Service Exchange Units In the event of a monitor malfunction due to electrical or electronic component failure it is our recommendation that a service exchange unit be ordered. The defective instrument should be returned to our works within 30 days of supplying the service exchange unit, then only the repair charge is payable. Otherwise the whole cost of a service exchange unit becomes payable. This procedure is by far the easiest and most cost effective way of ensuring the monitor on board conforms to I.M.O. resolution MEPhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7C.107 (49). Remark: According the MEPC.107(49) &#167; 4.2.11 the unit has to be checked at IOPP Certificate renewal survey by the manufacturer or persons authorized by the manufacturer. Alternatively the unit may be replaced by a calibrated 15 ppm Bilge Alarm. The OMD2005 is designed in that way, that only the measuring cell needs to be changed, as this unit carry the calibration onboard. The Calibration Certificate with the date of the last calibration check should be retained onboard for inspection purposes. If for some reasons the computer unit needs to be changed, it has to make sure, that the memory card will remain on board for at least 18 month. The new computer unit will carry its own memory card. The old card can be insert into the new unit only for reading. Writing is only possible with the card delivered with the new computer unit. For details see section 13.1.Issue: 12.11.04Instruction Manual OMD-2005Page 2 of 24http://www.51wendang.com/doc/ecdebe501974f24dedd356c7

DECKMA HAMBURG GmbHCONTENTSSECTION 1.0 2.0 3.0 3.1 3.2 3.3 3.4 4.0 5.0 6.0 7.0 8.0 8.1 9.0 10.0 10.1 10.2 10.3 10.4 11.0 11.1 12.0 12.1 13.0 13.1 14.0 14.1 15.0 15.1 16.0 Introduction Important Notes Principle of Operation Measuring Principle Features Adjustment Displays and Alarms Specification Construction Installation Piping Wiring Typical Control System Power Supply Commissioning Electrical Piping Functional Tests Programming Mode Operating Instructions Operator Notes Operator Maintenance Manual Cell Clean Unit Fault Finding Memory Card Calibration Calibration and Repeatability Check Spare Parts Recommended On Board Spares Remarks TITLE PAGE 4 4 4 4 5 5 5 7 8 9 10 11 13 13 13 13 13 14 15 17 18 18 19 20 21 22 22 23 23 24Issue: 12.11.04Instruction Manual OMD-2005Page 3 of 24

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0INTRODUCTION

OMD-2005 Bilge Alarm Unit has been designed specifichttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ally for use inconjunction with 15 ppm oil-water separator units and has a specification andperformance which exceeds the requirements of the International MaritimeOrganization specifications for 15ppm Bilge Alarms contained in ResolutionMEPC. 107 (49).

unit is supplied with 2 works-adjusted alarms at 15 ppm. Other set points(10 ppm or 5 ppm) are possible and can be adjusted on site at any time by usingthe buttons at the front panel.

an alarm set point is exceed, the alarms are visible at the front panel and theappropriate relays are switched. In case of malfunction the System LED at thefront panel will change from blinking green to permanent red and the appropriaterelay will switch the contacts.

the data logging function the unit requires an status input from the separatorand a feedback signal from the valve position limit switch. (See Fig. 1, Pos.6)

a 0(4) - 20 mA (equal to 0 - 30 http://www.51wendang.com/doc/ecdebe501974f24dedd356c7ppm) signal output is available fordriving a recorder or external meter.

.0IMPORTANT NOTES

)This equipment must be installed and operated in strict accordance with theinstructions contained in this manual. Failure to do so will impair the protectionprovided.

)Installation and servicing must be undertaken by a competent and suitableskilled person.

)The equipment must be connected to the ground according relevantrequirements.

)The unit must be isolated from the electrical supply before any maintenance ofthe equipment is attempted.

)All National or local codes of practice or regulations must be observed and,where applicable, are deemed to take precedence over any directive orinformation contained in this manual.

)In case of freezing conditions the measuring cell should be emptied complete.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0

.1PRINCIPLE OF OPERATIONhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7Measuring Principle

optical sensor array measure a combination of light scattered and absorbedby oil droplets in the sample stream. The sensor signals are then processed by amicroprocessor to produce linearised output.

an alarm (works set point 15 ppm) occurs, the two oil alarm relays are activatedafter the adjusted time delay.

microprocessor continuously monitors the condition of the sensorcomponents and associated electronics to ensure that calibration accuracy ismaintained over time and extremes of environmental conditions.

.2Features

Robust construction

Automatic voltage selection

Solid suppression capability

Low maintenance

Easy installation

Constant readiness

Low spare part stock holding

Watertight Housing

Works adjustment

Easy settings via menu

.3Adjustment

unit is delivered with ahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 works calibration according the IMO-requirements.The alarm points are set to 15 ppm.

&quot;Zero&quot; point is also works calibrated and can be re-adjusted on site by usingthe programming mode and clean water. See Section 10.4 “Service-Offset”. Acalibration is not permitted. This has to be done according IMO Regulations bythe manufacturer or persons authorized by the manufacturer.

.4Displays and Alarms

the unit are two independent oil alarm circuits available. Both can be setseparately from 1 to 15 ppm. From the manufacturing both alarms are set to15 ppm (according IMO). The set points can be changed according to therequirements on site, for example to 10 ppm or 5 ppm. An alarm point settingabove 15 ppm is not possible. The adjustment can be done in the programmingmode as described in Section 10.4.

this mode also the individual adjustment of the time delays for the alarms andthe possible changihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ng between 0 - 20 mA or 4 - 20 mA output can be done.

[此处图片未下载成功]

DECKMA HAMBURG GmbHBoth alarm circuits are also related to an alarm LED on the front panel.

case of malfunction the “System” LED will indicate any type of internal fault ofthe unit. This LED is flashing green in normal conditions and is red in alarmconditions. Also this alarm is related to an relay output.

to the alarm LED's each alarm circuit is equipped with a relay withpotential free alarm contacts. These contacts can be used for external processingof the signal or for control of further functions.

a malfunction or failure of the power supply occurs, all 3 relays will switch toalarm condition.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0SPECIFICATION OMD-2005Range:

Supply:

:

Points 1   2:

1 Ohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7perating Delay:

(for annunciation purpose)

2 Operating Delay:

(for control purposes)

Fault Alarm:

Contact Rating:

Indication:

Signal:

Water Pressure:

Flow:

Temperature:

Water Temperature:

:

(over all):

of Protection:

:

Connections:0 – 30 ppm, Trend up to 50 ppmAccording IMO MEPC. 107(49)Up to 30 ppm better than &#177; 2 %Green Graphic Display24 V – 240 V AC or DCAutomatic Voltage Selection&lt; 15 VAAdjustable between 1 - 15 ppm(Works adjustment 15 ppm)Adjustable between 1 – 540 sec.(Works adjustment 2 sec)Adjustable between 1 – 10 sec.(Works adjustment 10 sec)Red LEDPotential free 1 pole change overcontacts, 3 A / 240 VRed LED's0 – 20 mA or 4 – 20 mA for 0-30 ppmreversible, ext. Load &lt; 150  0,1 – 10 barApprox. 0,1 - 4 l/min depend. tohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 pressure  1 to   55&#176; C  1 to   65&#176; CUp to 45&#176;360 mm W x 240 mm H x 100 mm DIP 657,3 kgR &#188;&quot; Female

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0CONSTRUCTION

are 3 main parts which contained in an OMD-2005:

computer unit is mounted into an epoxy powder painted steel housingto protect the electronics of the display PCB with the data logger and themain board PCB with the terminals for external connections.

measuring cell is built out of an anodized all-aluminium body with inletand outlet block in stainless steel. This rugged cell contains the opticalelectronic and correspond with the computer unit via a plugged data cable.The valve assembly contains a special handle to sense the position of thevalve. This assembly is connected to the measuring cell by an easy tohandle fitting to enable the exchange of the cell for frequently adjustmentaccording the IMO requiremenhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ts.

components are mounted to a stainless steel mounting plate for easy wall orbulkhead installation. It is also possible to split the computer unit from themeasuring cell if the available space is not sufficient. For this version dividedmounting plates are available.

[此处图片未下载成功]

1

Computer UnitHead ScrewFittingMeasuring Cell5678HandleLimit SwitchSpacerValve Plate91011123/2 Way ValveMounting PlateDesiccatorCommunication CableFig. 1

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0INSTALLATION (Refer to Fig. 2 and Fig. 3)

Section 2 for important notes concerning installation.

OMD-2005 Monitor should be located as close as possible to the oily waterseparator to minimize response delays. According MEPC.107(49) the layout ofthe installation should be arranged so that the overall response time (includingthe response time of the 15 ppm Bilge Alarm) betweehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7n an effluent discharge fromthe 15 ppm Bilge Separator exceeding 15 ppm, and the operation of theAutomatic Stopping Device preventing overboard discharge, should be as shortas possible and in any case not more than 20 s.

the OMD-2005 Monitor by means of 6 x M8 screws on to a rigid verticalsurface and preferably with the display panel of the monitor at eye level. Forservice and maintenance sufficient space to all sides should be available.

must be taken at mounting of the pipes connections to avoid any torsion ofthe housing and damage of the instrument.

[此处图片未下载成功]

Fig. 2

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0PIPING (Refer to Fig. 3)

the OMD-2005 Monitor to the sample point of the oily-water separatoroutlet and to a source of oil free water employing 10 mm OD copper or stainlesssteel pipe. The sample point should be located on a vertical section of theseparahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7tor outflow piping to minimize the effects of any entrained air. The tappingpoint should be at a level above the outlet of the monitor to ensure the samplecell is flooded at all times.

connection to a vertical section of the separator outlet piping is impractical, thetapping may be made into the side of the horizontal pipe. Avoid top or bottomentry.

separator discharge pipes up to 75 mm OD a standard &quot;T&quot;-type junction ofthe welded or screwed type is satisfactory for the tapping point. For the separatordischarge pipes of 80 mm OD and above a sample probe should be employedwhich protrudes into the discharge piping by approx. 25 % of the ID of the pipe.

[此处图片未下载成功]

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0WIRING (Refer to Fig. 4   5)

Section 2 for important notes concerning wiring.

unit must be connected to the mains supply via a suitable rated andapprovedhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 fused isolator unless such fusing / isolation is provided by associatedequipment. When fitted, the isolator should be close, readily accessible andmarked as to function.

connections are made through the metric cable gland openings

[此处图片未下载成功]

prepared underneath the instrument.

. 4

wiring details will vary dependent upon the control system to beemployed but the most frequently used systems employ alarm relay 1 for alarmonly and alarm relay 2 for control purposes.

connections are made to the terminal blocks inside the computerhousing. Wires are connected to the terminals by pushing a suitable screwdriverinto the clamp holes to release the internal spring loaded clamps. After the wire isinserted to the terminal and the screwdriver is removed, the wire is fixed.

the instrument is operated at high voltages, additional care has to be taken toprovide rehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7liable ground connections. Ground (PE) can be connected direct to theterminal or, if this is not sufficient according local rules, to the computer housingleft side. In this case the plug needs to be replaced by a M6 screw with nut andrelated washers.

instrument provides a pilot voltage output at terminals 4&amp;5. This is internallyconnected to the power supply input (Terminals 1&amp;2), but is fused by Fuse F1 (2

). The pilot voltage can be used to supply additional external circuitry, e.g. alarmlamps or electrical valves.

note: any device connected to the pilot voltage output must be rated forthe voltage the instrument is supplied with. Do not use the pilot voltage for drivingmotors, heaters or other high load devices. The pilot voltage is intended for alarmpurposes only.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

. 5

front door complete after electrical installation. Whttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ater inside the instrument

result in corrosion and malfunction.

[此处图片未下载成功]

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.1Typical Control System

installation on site has to make sure that in case of any loss of power supplyand/or loss of air supply for the automatic stopping device the overboarddischarge valve close the overboard line and open the re-circulating line.

system showed in the example, employs alarm relay 2 to control apneumatic solenoid valve which energises or de-energises a pneumaticallyoperated 3 - way valve as depicted in Fig. 5.

separation process will continue until such time as the pollution level fallsbelow the alarm set point at which time the discharge will be directed overboard.

pump stop system is according MEPC.107 (49) not allowed.

.0POWER SUPPLY

Section 2 for important notes.

unit is designed for a powhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7er supply of 24 V to 240 V AC or DC. It has anautomatic power selection.

.0COMMISSIONING

Section 2 for important notes.

completion of the installation, wiring and piping carry out the following checks:10.1Electrical

) Check that the power supply is connected to the terminals 1   2 of the

block.

) Check the wiring of the automatic stopping device and to the alarm system is

the IMO Requirements.

)Check that the grounding has been made according to the relevantregulations.

.2Piping

)Check all piping connections for leaks and rectify as appropriate.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.3Functional Tests

)Run oil free water through the instrument to purge the system.

)Adjust the flow rate through the unit by using the small screws in the cell cap(Fig. 1, Pos. 2). Taking out a screw will increase thhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7e flow rate.

: The flow rate should be checked on both, the clean water supply and theseparator sample supply. If the clean water supply is obtained from a highpressure source, the flow rate will be higher than from the sample point.

flow rate is not influencing the accuracy of the instrument. The adjustmentis only important for the time delay between the sample point and the monitor.c) Switch on the instrument and make sure, that the Power LED is illuminated

the display is showing the

display for about 15

. After that time it will

to the standard display,

the actual

.

) During oil free water is running through the monitor check the Zero adjustmentaccording Section 11. The display should be &quot;0&quot; to “2” and the status will show“FW”. If the display varies by greater amounts, it may be that air entrainment ispresehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7nt. If this is the case, the cause must be located and rectified.

)If the Zero need to be adjusted, this can be done in the programming mode as

[此处图片未下载成功]

[此处图片未下载成功]

described in section 10.4. (Service – Offset)

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.4Programming Mode

the programming mode the alarm set points, the time delays, the signal outputand the zero can be modified. It is also possible to recall the factory default

at any time. The clock isfactory set for GMT, Greenwich MeanTime, and cannot be changed.There are 8 push buttons to controlthe functions of the display. In generalare the upper buttons for the datalogger and the lower buttons forchanging the display to the differentpages of the menu.

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

DECKMA HAMBURG GmbH

[此处图片未下载成功]

[此处图片未下载成功]

DECKMA HAMBURhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7G GmbHNB: All changed values have to be confirmed by pressing the &quot; OK &quot; button.Otherwise the existing values are valid.

.0 OPERATING INSTRUCTIONS

)Switch on the power supply.

)Allow a period of time for water entering the sample tube.

)Flow oil free water through the system for a few minutes and check that thedisplay show 0 to 2 ppm. If not, clean proper before adjusting the unitaccording section 10.4 “Service - Offset”.

)Switch the instrument sample supply from the clean water supply to theseparator sampling point connection.

)The instrument is now ready for use.

[此处图片未下载成功]

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.1Operator Notes

)When oily water flows through the instrument the display will show the actualvalue of oil content.

) If the oil concentration exceeds the adjusted threshold (works adjustment

ppm), the alarm ihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ndicator 1 will be illuminated in intervals during theselected time delay before it change to steady light and the associated alarmrelay will operate. Accordingly also the alarm indicator 2 will be illuminatedand its associated alarm relay will take the appropriate shut down action.

.0OPERATOR MAINTENANCE

Section 2 for important notes.

WEEKLY INTERVALS:

)Flush the cell with oil free water.

)Isolate the instrument from both, sample and oil free water supply.

)Unscrew and remove the cell cap.

)Insert a suitable Cell Cleaning brush (Art. No. 30102) into the cell and clean itwith upwards and downwards motion through the entire length of the cellseveral times.

)Remove the Cell Cleaning brush and replace the cell cap.

)Reconnect the oil free water supply and allow this to flow through theinstrument for a few minutes.

)Observe that the display is showing &http://www.51wendang.com/doc/ecdebe501974f24dedd356c7quot;0&quot; to “2”. If not, clean again.

)Examine the color of the desiccator (Fig. 1, Pos. 11). Blue color is indicatingan active moisture absorber. If the color is light blue or white, the desiccatorshould be replaced.

desiccator assures a humidity below 40% inside the measuring cell toavoid wrong measurement resulting due to condensation at the cell glass tubeand damage of the electronics around the glass tube. The replacement is easydone without opening the instrument. Just unscrew the old desiccator out ofthe front panel and replace it by a new one. The protection cap of the spareunit can be also used as a tool.

)Reconnect the instrument to the separator sampling point.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.1Manual Cell Clean Unit

item if fitted

unit facilitates cleaning of the cell without the need of removing the cell cap.Regular use of this device shttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7hould prevent malfunction of the monitor due simplyto fouling of the sample tube and all the inconvenience which this can cause.Operating Instructions

)Ensure that the monitor is switched off and that there is a clean water supplythrough the cell.

)Activate the manual cell clean unit by pressing the handle several times.c)Switch the monitor back on and check the reading is between 0 to 2 ppm.d)Repeat a) to c) at least once a week or as necessary.

: The Manual Cell Clean Unit may also be used during normal operation withsample water, but in this case an alarm occurs because the wiper is passing thelight source.

:  Wiper Seal, Part. No. 30605

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0FAULT FINDING

Section 2 for important notes.

OMD-2005 will indicate several malfunctions in the status line of the display.Pressing the “OK” button will lead into an informationhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 window, similar to the itemslisted in the table below.StatusReadingSystem-Alarm-

..49AlarmNormal

operation-Green /NoBlinkingGreen /No

-circuit 1,2ReasonServicingOKEESample reading is outof range:

content too high,

sample tubeWait until oil content iswithin the range,clean sample tube

-

sample, clean

tubeFW !Sample?0..49 / EEGreen /NoBlinkingEERed /SteadyYesAlarmAlarmFreshwater is enabledMeter is not able tomeasure the sample:

water in, oil content

too high, no light

possible

communication

computer unit

measuring cell

is not

:

DECKMA card in

is not

:

read only card is in

is not

:Com?EERed /Shttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7teadyYesAlarmCheck connectionbetween computerunit and measuringcellInsert the activememory cardInsert the activememory cardDatalog?0..49 / EERed /SteadyYesAlarmActivate card or insertthe active memory

new DECKMA card iscard

.ErrRed /

errorRestart the system

[此处图片未下载成功]

DECKMA HAMBURG GmbH

. 6

.1Memory Card (refer to Fig. 6)

Memory Card is located inside the door of the computer housing. It issuitable for the life of the instrument, as it is calculated to the according MEPC107(49) required storage time of at least 18 month. When the card is full, theoldest entry will be overwritten, so that a replacement is not necessary. Undernormal use the card should not be taken out, as this is linked with the specificsystem. The card can be read in other OMD-2005 units, but writing is onlypossible in the related system.

[此处图片未下载成功]://www.51wendang.com/doc/ecdebe501974f24dedd356c7r

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0CALIBRATION

ppm Bilge Alarms built according MEPC.107(49) have to be protected againstaccess beyond the checks of instrument drift, repeatability of the instrumentreading and zero adjustment. For this reason the instrument is electronicallysealed, so that only the manufacturer or his authorized persons, equipped withthe related tools, are able to get access for changing the calibration.

provide a simple procedure for check the instrument aboard ship, the OMD-2005 is constructed in that way, that the zero check also confirms the instrumentdrift within the specifications.

.1Calibration and repeatability check

)Switch off the power supply and stop any water flow.

)Clean the sample tube accurate by using a suitable cell cleaning brush asdescribed under Section 12.0. Make sure, that the offset is correct at &#177; 0.f)Run clean water http://www.51wendang.com/doc/ecdebe501974f24dedd356c7through the instrument.

)If it is sure, that non aerated, clean water is in the instrument, the readingshould be 0 ppm &#177; 2 ppm.

) Continue as described under Section 11.0.

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0SPARE PARTS

ordering spares, it is important to supply details of the type of monitor, partnumber of each spare required, its description and any relevant serial number.DESCRIPTION

Cleaning Brush

-Ring Set

,  T 2 A

,  T 1 AART-NUMBER65550301027577540107

Cell with Calibration Certificate75500/17500

.1Recommended On Board Spares

off Desiccator

off Cell Cleaning Brush

off O-Ring Set

off Fuse T 2 A65550301027577540107

item

off Manual Cell Clean Unit

[此处图片未下载成功]

DECKMA HAMBURG GmbH

.0REMARKS

the http://www.51wendang.com/doc/ecdebe501974f24dedd356c7modifications and deviations from the standard form, which have to becarried out in the supply, should be attached at this paragraph.

on: .............................             by: ..........................................                                      Date                                                   Firm's NameRemarks:

Date: 2004-09-22 JOWA 3SEP OWS Rev: A OILY WATER SEPARATOR Sign: GS Standard

.0 1.0m3/h and 2.5m3/h Pump Operating Manual K:1-NYA K1-JOWA PRODUKTER3SEP 36/41

1

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]://www.51wendang.com/doc/ecdebe501974f24dedd356c7

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

Dat

[此处图片未下载成功]

Date: 2004-09-22 JOWA 3SEP OWS

: A OILY WATER SEPARATOR

: GS Standard

.0 5.0m3/h Pump Operating Manual

:1-NYA K1-JOWA PRODUKTER3SEP 37/41

– Operation

: The following explanations have the aid to give you all possible informations over the Sidex pumps range. The right choising of the pump is depending from the right informations received at the order time. Those

received will be saved as the main job references for this pump.  Any application that will not be respecting our suggestions , will not be considered under any warranty possibility.

. General  1.1 Safety precautions  1.2 Health and http://www.51wendang.com/doc/ecdebe501974f24dedd356c7safety informations

. Unpacking , handling and storage   2.1 Unpacking   2.2 Handling

.3 Storage  3. Pump Description      4. Pump Installation

. Running Position    5.1 Preliminary actions

. Maintenance   6.1 Preliminary operations  6.2 Removing the stator 6.3 Removing the rotor 6.4 Removing the joint

. Problems , causes and remedies

General    1.1 Safety precautions

care following instructions , making in  the way that injury or damage to the pump can   be avoided becouse of non-payed attention.  Experienced personnel is required for the following phases:

* Always observe the techinical datas.

* Electrical connections MUST be followed by authorised personnel.   * Never start the pump in the wrong direction.Check every time before.  * Never put your fingers inside port connections. * Never touch the pump or pipeworks when pumping HOT – STEhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7RILIZED – TOXIC liquids. * Never run the pump with suction or delivery port blocked.

* Always disconnect the power supply when servicing the pump. * Always get free the pump from pipewoks pressure when maintening.    1.2 Health and satefy informations    The section gives informations on handling , storage and disposal of materials used in the

which may be considered hazardous to your health.  Keep every time your Safety Officer informed on all regulations.   If accidentally , hazardous substances are in touch with your skin or inhaled , then the   following precautions should be taken immediately :     SKIN : Wash with fresh water and soap

: Get out to fresh air immediately    EYES : Flush with fresh water , find a medical centre immediately

scheme is indicating you what used inside pump :  WHERE USED  LIQUID – PRODUCT  DANGER FOR   bearings anti-size compounds releases vapour  http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 stator-rotor  grease – vaselin hands and  skin  oil- general lubrication seal – gearbox eyes and skin

surface paint releases dust and fumes if  machined.  Treats as fire hazardous.

[此处图片未下载成功]

Unpacking , handling and storage    To avoid any problems ,when receiving your pump please follow this procedure :

- check delivery note against the good received - in a case pump has been ordered – delievered with drive , please check is relatives   instructions still available. Make immediately claiming if missing.

.1 Unpacking    We do consider this procedure really important and we suggest you to go ahead in this way

- inspect the packing if any possible damage happened during transit - with care , remove away the packing from the pump - just having a look on the pump , check any visible sign of damage - check drive also in a perfect conditions   2.2 Handlinghttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7

pumps weights , allow you to bring away the pump to the final destination without any   big problems.  Only when powered pump , we suggest you to use adeguate elevator.   2.3 Storage  After point 2.2 when pump has been inspected , in a case the pump will not be installed

, it has to be re-packed and placed in a suitable storage.  Points to be followed are :  place the pump in a good covered storage , dry place , and free from vibrations.  If pump is placed in a dusty atmosphere , a moisture repellent cover is necessary until the   pump is installed.  Move the pump weekly by rotating the drive train to prevent  block and bearings damage.

it is forecated very long time storage ( &gt; 6 months) , take away the stator alone and   protect it internally with adeguate grease.  Ask to our technical department which grease type has to be used.  Remove also drain plug (pos.51) to avoid vapour forming.://www.51wendang.com/doc/ecdebe501974f24dedd356c7ar

Pump description  The pump supplied , takes part to the “ VOLUMETRIC PUMP TYPE”.

main part of Sidex pump is the single helix metal rotor which rotates eccentrically   within a double helical resilient stator of twice the pitch lenght of the rotor.  The rotor of circular cross section creates a continuosly forming cavity as it rotates.  The cavity progresses towards the discharge port carrying the pumped liquid inside this   cavity by the continuosly forming of seal line .

flow is non-pulsating simply becouse stator ‘s chambre volume is always constant.    The pump will be considered therefore a positive displacement type with the follows   benefits : - self priming even no 100% liquid containing

- very low damage when hendling sensitive products - capacity is direct proportional to the pump speed  - possibility to handle viscous and abrasive material

- no pulsation     Also , duehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 to the peculiar Sidex pump system :

- no considereble torque increasing when reaching the top of the performance - low noise – vibrations - self-accomodating of the rotor eccentricity even under pressure - compact style construction

Pump installation    Pump must be installed in a horizontal position , leaving a space not less than 30 cm long all   around the pump. This will help you in making maintenance when the time and to get the   motor temperature as specification is requiring.

PORT

works have to be same size of delivery-discharge pump’s ports.    Just to help personnel to do servicing , will be very important to have a three –parts joint in   suction and discharge port.   When is forecasted a discharge liquid column &gt; 15 m , a non-back-flow valve will help you

avoid that pump-seal system could be overloaded by the water column.  If any dispositive will be mountehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7d on discharge pipe-work , a safety relief valve is suggested   to safe the pump from running against closed valve.    When pump is not fixed on the ground , a vibrating compensators are requested.

connections  All electrical connections , both for Sidex pump or any other machinery into which Sidex   pump is incorporated , MUST be followed by experienced personnel under the respect of   Machinery Directive and their relatives Amendmens.

[此处图片未下载成功]

[此处图片未下载成功]

Running position

: DRY RUN THE PUMP IS NOT PERMITTED.    Just few rounds will probably couse damage to the pumping parts, stator and rotor.   5.1 Few preliminary actions before run the pump :

* connect the pump to the both suction and delivery pipe-works * fill up the pump by water or the liquid will be handled just later on. The operation has to be   made it by using the port cloded with tap http://www.51wendang.com/doc/ecdebe501974f24dedd356c7, pos. 51.  After that , close the port with the same tap.  Note : The operation has to done just first time you start the pump.

* Nextly , pump will self-priming by itself.   * Before start with power supply , check any valve in the suction / delivery pipe-works is   opened. * Make the pump running for few seconds and verify if rotating sense is the RIGHT as well as   by the arrow signed over the lanter flange , pos. 10 or 11.

* In a case wrong electrical application , be in contact with qualified personnel and revise the   power supply connections.   *  Now , run the pump.

Maintenance   All maintenance operations MUST be done by qualified experienced personnel .    Sidex pump by the extremily semplified system of mounting and dismantling will allow you   to do servising and maintenance in a quick time with a good result.

our indications to avoid any mistakes.   6.1 Preliminary operationhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7s   Remove power supply from the motor’s pump.   Await liquid temperature goes down.   Verify no pressure in the suction or delivery pipe-work by checking eventually a manometer.

all valve in suction and discharge .  Remeove slowly pipe works from pump connections.      6.2 Removing the stator

.2.1 Unscrew the 4 screws (pos. 71/80 or 72/82 ) on the suction port. 6.2.2 Remove the suction port and STATOR (pos.03 ) will now be free to be removed also.  Check also the rotor now ( pos. 01) not demaged. 6.2.3 Take the new stator , lubricate it by liquid soap and insert the stator in the pump casing. 6.2.4 Close now by screwing the 4 screws previously removed.

.3 Removing the rotor

firstly operations explained before , 6.2.1   6.2.2.  6.3.1 After that , you need to disassamble the casing. Remove screws ( pos.80 or 71/81). 6.3.2 Take away delivery chambre (pos. 13).  Now you can see lantehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7rn flange with complete drive train.

.3.3 Remove metal protection ( pos. 90). 6.3.4 Block drive shaft (pos.20 ) on his head  by using adeguate spanner.  6.3.5 Insert a second spanner in the free lantern flange’s space , get the rotor with this spanner    and turn it anticlock wise direction. You get the rotor in your hands now. The joint   (pos. 05 )is free also to be replaced.

.4 Removing the joint  Joint is still connected to the drive shaft in one side , the other side is free becouse rotor   has been removed.  Screw a nut and relative counter-nut on this free threat in front of you.  Block them by rotating in opposite way each other.

now anti-clockwise direction the nut and the joint (pos. 05) will be free from drive   shaft.    Clean all parts arount it.

.5 Removing mechanical seal     Proceed following points 6.1 / 6.2 / 6.3 /6.4.   Just you took away the delivery chambre (pos.13) you can seehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 the mechamical seal free in

of you.  The first part you see is rotating face of mechanical seal.  Remove it from the drive shaft with care by using your hands only. No any tool is permitted   making this operation. Possibilities to demage this part of seal is high.  Clean it very well using a little warmed water.

, the fixed part of mechanical seal is fitted in the lantern flange (pos.10 or 11).  With care , by using an adeguate  screwdriver , remove the fixed mechanical seal part    making pressure firstly on one side and than in the other side.   The explanation was referred to the cast iron range where the fixed part of mechanical seal  is fitted inside to the lantern flange.   In a case stainless steel pump ,this opearation is much easier.

, just the delivery chambre has been removed , a stainless steel flange-seat is   keeping the mechanical seal in the right  working position.  Removing thhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7is flange-seat by unscrewing the four screws , the complete seal is free to be   cleaned or changed.

Problems, causes and remedies    A list of possibble problems amd relative remedies is attacched below.

.1 PROBLEM : PUMP DOESN’T START

.      A strange body could be located inside the Open the pump , verify situation and  pump. eventually take away the extraneous body.

doesn’t resist to the liquid handled. Check quotation and relative order.Eventually   replace stator type with the right one.  Liquid pumped is sedimenting and gets dry. Clean the pump every time you stop it.     Temperature too high and the stator is Get low temperature liquid.In a case not   blocking the rotor. possible , contact our techn, personnel.

.2 PROBLEM : PUMP DOESN’T SUCK

etc.     Stator is weared. Replace the stator according to this manual.

is weared.  Replace http://www.51wendang.com/doc/ecdebe501974f24dedd356c7the rotor according to this manual.   Verify if wearing is coming from abrasion or    corrosion.Change material eventually.     Mechanical seal is leaking. Replace the seal according to this manual.

.3 PROBLEM : UNDER CAPACITY AND PRESSURE

datas.      Too high pressure on delivery pipework. Misure by a pressure gauge and reduce

pressure eventually.     Air presence in the suction pipework. Check and close all screws in the suction pipe     Mechanical seal is leaking. Replace mechanical  seal.

pump is running dry. Fill up the casing , install a dispositiv against   dry running.  Stator is weared. Replace stator.  Rotor is weared. Replace rotor.     Suction lift too big, Reduce pipe loss by increasing suction pipe

.Keep the suction port closer to the liquid   level.

.4 PROBLEM : PUMP IS NOISING

stator Replace the stator

rotor. Replhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ace the rotor.     Weared joint.  Replace the joint.

presence in the pipesworks. Increase liquid level on the suction side.       7.5 PROBLEM : PUMPING ELEMENTS WEAR

high pressure. Use a manometer-pressure gauge to keep

pressure under controll.     Too high liquid temperature. Reduce liquid temperature.   In a case no possible, contact our personnel.     Liquid handled is stopping inside pump. Open and clean the pump all the time you

it.     Pump is running dry. Fill up the pump first time you use it.   Install a correct running dry dispositive.

Range - Sizes 254 /354 / 504 / 604 /1004 Cast Iron

. Q.ty Description

1

1

1

1

1 16 1

1

1

1

2 45 4

4

2

2

2 71 4

4

4

4

1

1 Rotohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7r Stator Joint Lantern flange Delivery chambre Suction

[此处图片未下载成功]

port Female drive shaft O-Ring Mechanical seal Washer ,Joint Washer Washer  Drain Plug Grub Screw Nut Screw Screw Nut Nut  Metal Protection Splash Guard Ring CODING

Date

[此处图片未下载成功]

Date: 2004-09-22 JOWA 3SEP OWS

: A OILY WATER SEPARATOR

: GS Standard

.0 10.0m3/h Pump Operating Manual

:1-NYA K1-JOWA PRODUKTER3SEP 38/41

– Operation

:

following explanations have the aid to give you all possible information over the SYDEX pumps range. The right choosing of the pump is depending from the right information received at the order time. Those information received will be saved as the main job references for this pump.

application that will not be respecting our suggestiohttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ns, will not be considered under any warranty possibility.

. General

.1 Safety precautions

.2 Health and safety information

. Unpacking, handling and storage

.1 Unpacking

.2 Handling

.3 Storage

. Pump Description

. Pump Installation

. Running Position

.1 Preliminary actions

. Maintenance

.1 Preliminary operations

.2 Removing the stator

.3 Removing the rotor

.4 Removing the joint

. Problems, causes and remedies

General

.1 Safety precautions

care following instructions, making in the way that injury or damage to the pump can

avoided because of non-payed attention.

personnel is required for the following phasehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7s:

* Always observe the technical datas.

* Electrical connections MUST be followed by authorised personnel.

* Never start the pump in the wrong direction. Check every time before.  * Never put your fingers inside port connections.

* Never touch the pump or pipeworks when pumping HOT – STERILIZED – TOXIC liquids.

* Never run the pump with suction or delivery port blocked.

* Always disconnect the power supply when servicing the pump.

* Always get free the pump from pipewoks pressure when maintaining.

.2 Health and safety information

section gives information on handling, storage and disposal of materials used in the

which may be considered hazardous to your health.

every time your Safety Officer informed on all regulations.

accidentally, hazardous substances are in touch with your skin or inhaled, then the://www.51wendang.com/doc/ecdebe501974f24dedd356c7arprecautions should be taken immediately:

:  Wash with fresh water and soap

:  Get out to fresh air immediately

:  Flush with fresh water, find a medical centre immediately

scheme is indicating you what used inside pump:  WHERE USED  LIQUID – PRODUCT  DANGER FOR   Bearings anti-size compounds releases vapour   Stator - rotor  grease – Vaseline hands and  skin  Oil - general lubrication seal – gearbox eyes and skin

surface Paint releases dust and fumes if

.

as fire hazardous.

Unpacking , handling and storage

avoid any problems, when receiving your pump please follow this procedure:

- check delivery note against the good received

- in a case pump has been ordered – delievered with drive, please check is relatives

still availablehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7. Make immediately claiming if missing.

.1 Unpacking

[此处图片未下载成功]

We do consider this procedure really important and we suggest you to go ahead in this way

- inspect the packing if any possible damage happened during transit

- with care, remove away the packing from the pump

- just having a look on the pump , check any visible sign of damage

- check drive also in a perfect conditions

.2 Handling

pumps weights, allow you to bring away the pump to the final destination without any

problems.  Only when powered pump, we suggest you to use adequate elevator.

.3 Storage

point 2.2 when pump has been inspected, in a case the pump will not be installed

, it has to be re-packed and placed in a suitable storage.

to be followed are:

the pump in ahttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 good covered storage, dry place, and free from vibrations.  If pump is placed in a dusty atmosphere, a moisture repellent cover is necessary until the

is installed.

the pump weekly by rotating the drive train to prevent block and bearings damage.

it is forecasted very long time storage (&gt; 6 months), take away the stator alone and

it internally with adequate grease.

to our technical department which grease type has to be used.

also drain plug (pos.51) to avoid vapour forming.

Pump description

pump supplied, takes part to the “ VOLUMETRIC PUMP TYPE”.

main part of SYDEX pump is the single helix metal rotor which rotates eccentrically

a double helical resilient stator of twice the pitch length of the rotor.  The rotor of circular cross section creates a continuously forming cavity as it rotates.://www.51wendang.com/doc/ecdebe501974f24dedd356c7cavity progresses towards the discharge port carrying the pumped liquid inside this

by the continuously forming of seal line .

flow is non-pulsating simply because stator‘s chamber volume is always constant.

pump will be considered therefore a positive displacement type with the follows   Benefits:

- self priming even no 100% liquid containing

- very low damage when handling sensitive products

- capacity is direct proportional to the pump speed

- possibility to handle viscous and abrasive material

- no pulsation

, due to the peculiar SYDEX pump system : - no considerable torque increasing when reaching the top of the performance

- low noise – vibrations

- self-accomodating of the rotor eccentricity even under pressure

- compact style construction

Pump installation

musthttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7 be installed in a horizontal position, leaving a space not less than 30 cm long all

the pump. This will help you in making maintenance when the time and keep motor’ s

as low as motor’s specifications.

works have to be same size of delivery-discharge pump’s ports.

to help personnel to do servicing, will be very important to have a three –parts joint in

and discharge port.

is forecasted a discharge liquid column &gt; 15 m , a non-back-flow valve will help you

avoid that pump-seal system could be overloaded by the water column.

any dispositive will be mounted on discharge pipe-work, a safety relief valve is suggested

safe the pump from running against closed valve.

pump is not fixed on the ground, a vibrating compensators are requested.

://www.51wendang.com/doc/ecdebe501974f24dedd356c7arElectric connections

electrical connections, both for SYDEX pump or any other machinery into which SYDEX

is incorporated , MUST be followed by experienced personnel under the respect of   Machinery Directive and their relatives Amendments.

Running position

: DRY RUN THE PUMP IS NOT PERMITTED.

few rounds will probably cause damage to the pumping parts, stator and rotor.

.1 Few preliminary actions before run the pump:

* connect the pump to the both suction and delivery pipe-works

* fill up the pump by water or the liquid will be handled just later on. The operation has to be

it by using the port closed with tap , pos. 51.

that, close the port with the same tap.

: The operation has to done just first time you start the pump.

* Nextly, pump will self-priming by itself.

* Before sthttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7art with power supply, check any valve in the suction / delivery pipe-works is

.

*

[此处图片未下载成功]

Make the pump running for few seconds and verify if rotating sense is the RIGHT as well as   DISCHARGE 5

the arrow signed over the lantern flange , pos. 10 or 11.

* In a case wrong electrical application, be in contact with qualified personnel and revise the

supply connections.

*  Now, run the pump.

Maintenance

maintenance operations MUST be done by qualified experienced personnel.

pump by the extremely simplified system of mounting and dismantling will allow you   to do servicing and maintenance in a quick time with a good result.

our indications to avoid any mistakes.

.1 Preliminary operations

power supply from the motor’s pump.

lihttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7quid temperature goes down.

no pressure in the suction or delivery pipe-work by checking eventually a manometer.  Close all valve in suction and discharge.

slowly pipe works from pump connections.

.2 Removing the stator

.2.1 Unscrew the 4 screws (pos. 71/80 or 72/82) on the suction port.

.2.2 Remove the suction port and STATOR (pos.03) will now be free to be removed also.  Check also the rotor now (pos. 01) not damaged.

.2.3 Take the new stator, lubricate it by liquid soap and insert the stator in the pump casing.

.2.4 Close now by screwing the 4 screws previously removed.

.3 Removing the rotor

firstly operations explained before, 6.2.1   6.2.2.

.3.1 After that, you need to disassemble the casing. Remove screws (pos.80 or 71/81).

.3.2 Take away delivery chamber (pos. 13).

you can see lantern http://www.51wendang.com/doc/ecdebe501974f24dedd356c7flange with complete drive train.

.3.3 Remove metal protection (pos. 90).

.3.4 Block drive shaft (pos.20) on his head by using adequate spanner.

.3.5 Insert a second spanner in the free lantern flange’s space, get the rotor with this spanner

turn it anticlock wise direction. You get the rotor in your hands now. The joint   (pos. 05)is free also to be replaced.

.4 Removing the joint

is still connected to the drive shaft in one side, the other side is free because rotor

been removed.

a nut and relative counter-nut on this free threat in front of you.  Block them by rotating in opposite way each other.

now anti-clockwise direction the nut and the joint (pos. 05) will be free from drive

.

all parts around it.

.5

.1

.2

http://www.51wendang.com/doc/ecdebe501974f24dedd356c7

mechanical seal   Proceed following points 6.1 / 6.2 / 6.3 /6.4.  Just you took away the delivery chamber (pos.13) you can see the mechanical seal free in  front of you. The first part you see is rotating face of mechanical seal. Remove it from the drive shaft with care by using your hands only. No any tool is permitted  making this operation. Possibilities to damage this part of seal is high. Clean it very well using a little warmed water. Now, the fixed part of mechanical seal is fitted in the lantern flange (pos.10 or 11). With care, by using an adequate screwdriver, remove the fixed mechanical seal part   making pressure firstly on one side and than in the other side.  The explanation was referred to the cast iron range where the fixed part of mechanical seal is fitted inside to the lantern flange.  In a case stainless steel pump, this operation is much easier.  Infact, just the delivery chamber has been removed,http://www.51wendang.com/doc/ecdebe501974f24dedd356c7 a stainless steel flange-seat is  keeping the mechanical seal in the right  working position. Removing this flange-seat by unscrewing the four screws, the complete seal is free to be  cleaned or changed.   Problems, causes and remedies  A list of possible problems and relative remedies is attached below.   PROBLEM: PUMP DOESN’T START   Type of motor is Not adequate to the local Check motor and net datas. net.    A strange body could be located inside the Open the pump, verify situation and pump. eventually take away the extraneous body.   Stator doesn’t resist to the liquid handled. Check quotation and relative order. Eventually  replace stator type with the right one. Liquid pumped is sedimenting and gets dry. Clean the pump every time you stop it.   Temperature too high and the stator is Get low temperature liquid. In a case not  blocking the rotor. possible, contact our techn, personnel.      PROBLEM : PUMP DOESN’T SUCK  Suction http://www.51wendang.com/doc/ecdebe501974f24dedd356c7pipework is open. Check all gaskets and screw well all the nuts,  screw etc.   Stator is weared. Replace the stator according to this manual.   Rotor is weared.  Replace the rotor according to this manual.  Verify if wearing is coming from abrasion or  7

.3

.4

.5

seal is leaking.   PROBLEM : UNDER CAPACITY AND PRESSURE  Electrical motor datas are not correct facing net datas.  Too high pressure on delivery pipework.   Air presence in the suction pipework.  Mechanical seal is leaking. Sometimes pump is running dry.  Stator is weared. Rotor is weared. Suction lift too big,    PROBLEM: PUMP IS NOISING   Weared stator  Weared rotor.  Weared joint.   Air presence in the pipesworks.    corrosion. Change material eventually.  Replace the seal according to this manual.   Check order datas and installation system.   Misure by a pressure gauge and reduce  line preshttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7sure eventually.  Check and close all screws in the suction pipe  Replace mechanical seal. Fill up the casing, install a dispositive against dry running. Replace stator. Replace rotor. Reduce pipe loss by increasing suction pipe work. Keep the suction port closer to the liquid level.   Replace the stator  Replace the rotor.  Replace the joint.   Increase liquid level on the suction side.   PROBLEM: PUMPING ELEMENTS WEAR Too high pressure.   Too high liquid temperature.   Liquid handled is stopping inside pump.   Use a manometer-pressure gauge to keep  delivery pressure under control.  Reduce liquid temperature. In a case no possible, contact our personnel.  Open and clean the pump all the time you  stop it.  8

is running dry.   Fill up the pump first time you use it. Install a correct running dry dispositive.

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

://www.51wendang.com/doc/ecdebe501974f24dedd356c7Pos.

.ty 01 01 01 06 02 DENOMINATION / DESCRIPTION BLOCK LANTERN SUCTION CHAMBERDISCHARGE FLANGEFEMALE DRIVE SHAFT CONNECTING RODROTORSTATORMECHANICAL SEAL DRAIN PLUG SPACER RINGORING LANTERNSPLASH GUARD RINGCONNECTOR TIE ROD SUPPORT FOOTSCREW JOINTNUTWASHER SCREWSCREW LANTERNCODING      CREWNUTPROTECTION

Date: 2004-09-22 JOWA 3SEP OWS Rev: A OILY WATER SEPARATOR Sign: GS Standard

.0 Oil Sensor Operating Manual

:1-NYA K1-JOWA PRODUKTER3SEP 39/41

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

Date: 2004-09-22 JOWA 3SEP OWS Rev: A OILY WATER SEPARATOR Sign: GS Standard

.0 Spare/ Consumables Parts List  K:1-NYA K1-JOWA PRODUKTER3SEP 40/41

JOWA 3SEP OWS Spares Rev A

://www.51wendang.com/doc/ecdebe501974f24dedd356c7ded Consumables and Spareparts for JOWA 3SEP OWS 1.0m3/h

:00

:01

:02

:03

:04

:00

:01

:02

:03

:04

:05

:06

:07

:08

:09

:10

:11

:12

:13

:14

:15

:16

:17Article NoDescriptionStart UpQuantity1 year3 yearsCOMSUMABLES:17004-12407Jowa F-200C Filter material20013-02500Zinc Anode 1-5m3 Filter Tanks20013-70800Zinc Anode 10m3 Filter Tanks20013-02500Zinc Anode Gravity TankSPAREPARTS:50075-22002Filterscreen top 1.0mm50100-21002Filterscreen bottom 0.5mm50075-21002Filterscreen Drain 0.5mm22311-03600Oil Sensor Stick CLM-36N10109-00002Pressure gauge 0-10 BAR P194007-52010Fuse 1 A27060-20202Main Switch KG2027060-42001Power On CG4 A178727060-421021-0-2 Switch CG4 A21020610-01042Reset Push Button 20600-00110OPLC M91-2-R120600-00111Epander Phttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7LC EX90-D18-R0842000-00230Relay PT37073099100-00203Relay 3RT1017 1AP01 5,5kW99100-00018Terminals WDU 2,520700-75552Transformer 380-480/2X11099100-00086Transformer 230VAC/24V DC5011150111150kg111111111011111111111111111101003:00RTE OIL CONTENT METER

:0187081-00000JOWA RTE Oil Content Meter

:00

:01

:02

:03

:00

:01

:02

:03

:04

:05

:06

:07PUMP23001-0001222415-0000222415-00001VALVES22304-0025622304-0032622304-0040622304-0623650000-6000322303-2501510107-084361Stator Mono CggO ring mono pump G rangeMechanical Seal111Pneumatic valves DN25Pnematic valves DN32 Pnematic valves DN40Solenoid valves completeSafety valve DN15 6 BAR Safety valve DN25 6 BARPressure Gauge Valve DN151111111

:1-NYA K1-JOWA PRODUKTER3SEPParts List\par

Recommended Consumables and Spareparts for

3SEP OWS 2http://www.51wendang.com/doc/ecdebe501974f24dedd356c7.5m3/h

NoDescriptionStart UpQuantity1 year3 years

:00COMSUMABLES:

:0217004-12407

:00

:01

:02

:03

:04

:05

:06

:07

:08

:09

:10

:11

:12

:13

:14

:15

:16

:17SPAREPARTS:50150-2200250150-2200250075-2100222311-0360010109-0000294007-5201027060-2020227060-4200127060-4210220610-0104220600-0011020600-0011142000-0023099100-0020399100-0001820700-7555299100-00086Jowa F-200C Filter material100100300kgFilterscreen top 1.0mmFilterscreen bottom 0.5mmFilterscreen Drain 0.5mmOil Sensor Stick CLM-36NPressure gauge 0-10 BAR P1Fuse 1 AMain Switch KG20Power On CG4 A17871-0-2 Switch CG4 A210Reset Push Button OPLC M91-2-R1Epander PLC EX90-D18-R08Relay PT370730Relay 3RT1017 1AP01 5,5kWTerminals WDU 2,5Transformer 380-480/2X110Transformer 230VAC/24V DC111111011111111http://www.51wendang.com/doc/ecdebe501974f24dedd356c71111111111010

:00RTE OIL CONTENT METER

:0187081-00000JOWA RTE Oil Content Meter

:00

:01

:02

:03

:00

:01

:02

:03

:04

:05

:06

:07PUMP23002-0001222415-0000222415-00001VALVES22304-0025622304-0032622304-0040622304-0623650000-6000322303-2501510107-084361Stator Mono CghO ring mono pump G rangeMechanical Seal111Pneumatic valves DN25Pnematic valves DN32 Pnematic valves DN40Solenoid valves completeSafety valve DN15 6 BAR Safety valve DN25 6 BARPressure Gauge Valve DN151111111

Recommended Consumables and Spareparts for JOWA 3SEP OWS 5.0m3/h

No

:00COMSUMABLES:

:0217004-12407

:00

:01

:02

:03

:04

:05

:06

:07

:08

:09

:10

:11

:12

:13

:14

:http://www.51wendang.com/doc/ecdebe501974f24dedd356c715

:16

:17SPAREPARTS:50150-2200250150-2200250075-2100222311-0360010109-0000294007-5201027060-2020227060-4200127060-4210220610-0104220600-0011020600-0011142000-0023099100-0020399100-0001820700-7555299100-00086DescriptionStart UpQuantity1 year3 yearsJowa F-200C Filter material200200600kgFilterscreen top 1.0mmFilterscreen bottom 0.5mmFilterscreen Drain 0.5mmOil Sensor Stick CLM-36NPressure gauge 0-10 BAR P1Fuse 1 AMain Switch KG20Power On CG4 A17871-0-2 Switch CG4 A210Reset Push Button OPLC M91-2-R1Epander PLC EX90-D18-R08Relay PT370730Relay 3RT1017 1AP01 5,5kWTerminals WDU 2,5Transformer 380-480/2X110Transformer 230VAC/24V DC111111011111111111111111101003:00RTE OIL CONTENT METER

:0187081-00000JOWA RTE Oil Content Meter

:00

:01

:02

:03

:00

:01

:02

:03

:04

:05

:06

:07PUMP22440-0060122440-0060522440-00602Vhttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7ALVES22304-0025622304-0032622304-0040622304-0623650000-6000322303-2501510107-084361Stator 1O ring 1Mechanical Seal1Pneumatic valves DN25Pnematic valves DN32 Pnematic valves DN40Solenoid valves completeSafety valve DN15 6 BAR Safety valve DN25 6 BARPressure Gauge Valve DN151111111

Recommended Consumables and Spareparts for JOWA 3SEP OWS 10.0m3/h

No

:00COMSUMABLES:

:0217004-12407

:00

:01

:02

:03

:04

:05

:06

:07

:08

:09

:10

:11

:12

:13

:14

:15

:16

:17SPAREPARTS:50150-2200250150-2200250075-2100222311-0360010109-0000294007-5201027060-2020227060-4200127060-4210220610-0104220600-0011020600-0011142000-0023099100-0020399100-0001820700-7555299100-00086DescriptionStart UpQuantity1 year3 yearsJowa F-200C Filter material5005001500kgFilterscrehttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7en top 1.0mmFilterscreen bottom 0.5mmFilterscreen Drain 0.5mmOil Sensor Stick CLM-36NPressure gauge 0-10 BAR P1Fuse 1 AMain Switch KG20Power On CG4 A17871-0-2 Switch CG4 A210Reset Push Button OPLC M91-2-R1Epander PLC EX90-D18-R08Relay PT370730Relay 3RT1017 1AP01 5,5kWTerminals WDU 2,5Transformer 380-480/2X110Transformer 230VAC/24V DC111111011111111111111111101003:00RTE OIL CONTENT METER

:0187081-00000JOWA RTE Oil Content Meter

:00

:01

:02

:03

:00

:01

:02

:03

:04

:05

:06

:07PUMP24400-0110124400-0110524400-01102VALVES22304-0025622304-0032622304-0040622304-0623650000-6000322303-2501510107-084361Stator 1O ring 1Mechanical Seal1Pneumatic valves DN25Pnematic valves DN32 Pnematic valves DN40Solenoid valves completeSafety valve DN15 6 BAR Safety valve DN25 6 BARPressure Gauge Valve DN151111111

Date: 2004-09-22 JOWA 3Shttp://www.51wendang.com/doc/ecdebe501974f24dedd356c7EP OWS Rev: A OILY WATER SEPARATOR Sign: GS Standard

.0 Approval Certificates

[此处图片未下载成功]

1

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 https://www.51wendang.com/

亿万文档资料，等你来发现