本文档下载自文档下载网，内容可能不完整，您可以点击以下网址继续阅读或下载：

http://www.wendangwang.com/doc/efe960bed681037ac6d62544

OSAI系统CNC编程手册CHS-135

用OSAI系统编程的 不得不看

[此处图片未下载成功]

系列 CNC编程手册

编号：45004457K 版本：18 版权所有:

Electro Spa

版本：: 2011 年1 2月

本手册是为了供Prima Electro 公司使用而准备的，其描述了发布的最新产品信息。Prima Electro 公司有权在任何时间，无需事先通知，修改、改进在本手册内描述的产品。对本产品的实际操作取决于用户. Prima Electro 不对任何可能由安装或使用手册中描写的设备而造成的间接损坏负责。

并非所有章节被翻译成为中文，英文版手册仍然是官方正式版。

2012 - Prima Electro S.p.A. All rights reserved.

Electro S.p.A.

of manual

版本 00

日期 10/03/2012

备注

编译者 James

K

[此处图片未下载成功]

目录

. 前言 ..................................................................................................................................................... 9 2. 10系列系统编程 ............................................................................................................................... 11

.1 2.2

程序文件 ............................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544........................................................................................................................ 11 程序组成 .................................................................................................................................................................................... 11

. 轴编程 ............................................................................................................................................... 22

.1

轴运动编码 ................................................................................................................................................................................ 22

定义轴运动 .............................................................................................................................................. 22

.1.1 3.2 3.3 3.4 3.5 3.6 3.7

–快速轴定位 .....................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544............................................................................................................... 22 G01 – 直线插补 ....................................................................................................................................................................... 24 G02 G03 – 圆弧插补 .............................................................................................................................................................. 25 CET (PRC) – 圆弧终点容许值 ............................................................................................................................................ 27 FCT – 整圆缝合临界值 ......................................................................................................................................................... 27 ARM – 圆弧修正模式 ...........................................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544.................................. 28

.8 CRT – Circular interpolation spped reeducstion threshold                              CRK – Circular interpolation

reduction constant ..................................................................................................................................................................... 32 3.9 3.10 3.11 3.12 3.13 3.14 3.15 3.16 3.17 3.18 3.19 3.20 3.21 3.22 3.23

螺旋状插补 ................................................................................................................................................................................ 34 G33 – 等螺距或者变螺距螺纹加工 .................................................................................................................................. 35 旋转轴 ............................................................................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544............................. 39 循环轴 ......................................................................................................................................................................................... 39 Pseudo Axes.......................................................................................................................................... 错误！未定义书签。 Diameter Axes .......................................................................................................................................................................... 41 UDA - 双轴 ........................................................................................................................................................................... 44 SDA – Special Dual Axes ........................................................................................................................................................ 45 XDA – Mhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544aster/Slaves axes ..................................................................................................................................................... 46 AXF – Definition of axes with dynamic following function ........................................................................................... 54 CPA – Read/Write of a CNC parameter related to an axis ......................................................................................... 56 CPD – Drive Parameters Read/Write ................................................................................................................................ 59 工作原点和坐标控制码......................................................................................................................................................... 61 G17 G18 G19 -  选择插补平面 .......................................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544............... 62 G16 -  定义插补平面 ......................................................................................................................................................... 62

.25 3.26 3.27 3.28 3.29 3.30 3.31 3.32 3.33 3.34 3.35 3.36 3.37 3.38 3.39 3.40 3.41 3.42 3.43 3.44 3.45 3.46 3.47 3.48 3.49 3.50 3.51 3.52 3.53 3.54 3.55 3.56 3.57

– 减速前瞰 .................................................................................................................................................................. 67 DYM – Dynamic Mode ............................................................................................................................................................ 68 MDA – 最大减速角度 ............................................................................................................................................................ 69 VEF – Velocity Factor .........................http://www.wendangwang.com/doc/efe960bed681037ac6d62544..................................................................................................................................... 70 CRV – Curve – Feed rate optimization parameter ......................................................................................................... 72 MOA – Motion Auxiliary ........................................................................................................................................................ 73 Jerk Limitation ........................................................................................................................................................................... 73 MOV – Enable Jerk Limitation ............................................................................................................................................... 74 JRK – Jerk Time Constant .................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544..................................................................... 82 JRS – Jerk Smooth Constant .................................................................................................................................................. 83 ODH – Online Debug Help .............................................................................................................. 错误！未定义书签。 MBA – MultiBlock retrace Auxiliary functions .................................................................................................................. 84 REM – Automatic return to profiled at end of move ..................................................................................................... 85 IPB (DTL) – In Position Band................................................................................................................................................. 85 MOM – Manual Operating Modality .......................http://www.wendangwang.com/doc/efe960bed681037ac6d62544............................................................................................................. 86 G70 G71 -  测量单位.............................................................................................................................................................. 89 G90 G91 G79 – 绝对，增量和归零点编程 ................................................................................................................ 90 G92 G98 G99 – Axis Presetting ........................................................................................................................................... 92 G04 G09 – 程序段尾部延时和减速 .................................................................................................................................. 93 t -  程序段执行时间 ............................................................................................................................................................... 94 DWT (TMR)http://www.wendangwang.com/doc/efe960bed681037ac6d62544 – 停顿时间 ....................................................................................................................................................... 94 G93 – V/D进给率 ............................................................................................................................................................... 95 VFF -  前馈 ................................................................................................................................................................................. 96 SCF – 刻度比例因数 ............................................................................................................................................................... 97 MIR -  镜像加工 ................................................................................................................................................................... 98 ROT (URT) – 插补平面旋转 .........................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544................................................................................................ 100 UAO – 使用工作原点 .......................................................................................................................................................... 103 UTO (UOT) – 使用临时原点 ............................................................................................................................................ 104 UIO – Using Incremental Origin......................................................................................................................................... 106 RQO – Requalifying Origins ............................................................................................................. 错误！未定义书签。 SOL (DLO) -  软超行程 .................................................................................................................................................. 109 DPA (DSA) – 定义保护区域 .http://www.wendangwang.com/doc/efe960bed681037ac6d62544......................................................................................................................................... 110 PAE (ASC) – 激活保护区域 ........................................................................................................................................... 111

.59

AXES MANAGEMENT ................................................................................................... 错误！未定义书签。

Axes ............................................................................................................................................. 112 Virtual modes available on 10 Series CNC .............................................................................................. 112 Programming .......................................................................................................................................... 169

.59.1 3.59.2 3.60 http://www.wendangwang.com/doc/efe960bed681037ac6d625443.61 3.62 3.60.1

- Rotation of Cartesian axes ...................................................................................................................................... 113 TCP - Tool Center Point for machines with Prismatic Head ..................................................................................... 170 ANGULAR TRANSMISSION .............................................................................................................................................. 175

transmission table ..................................................................................................................... 176 Programming .......................................................................................................................................... 178 TPC table for machines with “Mixed” head ..................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544.......... 179 Rotary axes table .................................................................................................................................... 180 TCP table for machines with head “MachineBed ................................................................................... 184 Rotary axes table .................................................................................................................................... 186 TCP on multi-processor ........................................................................................................................... 189 REMARKS ON TCP PARAMETERS Dynamic Mode – L356 ........................................................................ 189 Operational Limits Mode – L367 ............................................................................................................. 190

.62.1 3.62.2 3.63 3.63.1 3.63.2 3.64 3.64.1 3.64.2 3.64.3 3.http://www.wendangwang.com/doc/efe960bed681037ac6d6254464.4 3.64.5

- Tool Center Point for machines with rotary axis plus balancing axis (Mixed) .......................................... 179

- Tool Center Point for machines with double rotary axis on the table (MachineBed) ............................ 183

. 刀具和刀具补偿编程 ...................................................................................................................... 191

.1 4.2 4.3 4.4 4.5 4.6 4.7 4.8 4.9

用于刀具编程的T字母 ...................................................................................................................................................... 191 用于多刀具编程的T字母 .................................................................................................................................................. 192 h 字母 ...............................................................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544......................................... 194 TTR – 平头刀尖 Radius ....................................................................................................................................................... 196 AXO – Axis Offset Definition ............................................................................................................................................. 196 RQT – Requalifying Tool Offset ......................................................................................................................................... 198 RQP – Requalifying Tool Offset .......................................................................................................................................... 199 TOU(TOF) – Tool Expiry Declaration ............................................................................................................................. 199 LOA – Table Loading ..................http://www.wendangwang.com/doc/efe960bed681037ac6d62544........................................................................................................................................... 200

. 刀具直径补偿 .................................................................................................................................. 201

.1 5.2 5.3 5.4 5.5 5.6 5.7

– Tool Type Compensation ....................................................................................................................................... 202 G40 G41 G42 – 刀具直径补偿G代码 ........................................................................................................................... 203 r – 补偿轮廓中的半径 ......................................................................................................................................................... 216 b – 补偿轮廓上的斜面 ......................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544................................................... 217 TPO – Path optimisation on bevels with G41(G42 ....................................................................................................... 219 TPA – Threshold angle for TPO ......................................................................................................................................... 229 TPT – Tool Path Threshold ................................................................................................................................................. 230

.8 5.9 5.10 5.11 5.12

v w – Paraxial Compensation .......................................................................................................................................... 231 UVW – Definition of axes for paraxial compensation .................................................................................................. 235 MSA (UOV) – Defining ahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 Machining Stock Allowance .................................................................................................. 236 GTP – Get Point ..................................................................................................................................................................... 238 CCP – Cutter Compensation Profile ................................................................................................................................ 241

. 主轴的编程 ...................................................................................................................................... 242

.1 6.2 6.3 6.4

G97 – CSS和RPM编程 ............................................................................................................................................. 242 SSL – 主轴速度限制 ..................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544............................................................ 243 M19 - Oriented Spindle Stop M19 – 指定方向的轴停止 ........................................................................................... 244 GTS – Spindle sharing ............................................................................................................................................................ 245

. M代码 ............................................................................................................................................. 246

.1

标准M代码 ............................................................................................................................................................................. 246

. 一些变量的相关应用 ...................................................................................................................... 249

.1 8.2 8.3 8.4 8.5 8.6 8.7 8.8

变量 ..http://www.wendangwang.com/doc/efe960bed681037ac6d62544...................................................................................................................................................................................... 252 ! – User variables .................................................................................................................................................................... 253 SN – 系统数字 ........................................................................................................................................................................ 255 SC – 系统字符 ........................................................................................................................................................................ 256 TIM – 系统计时器 ................................................................................................................................................................. 257 @ - PLUS变量 ...............http://www.wendangwang.com/doc/efe960bed681037ac6d62544......................................................................................................................................................... 257 L 变量 ........................................................................................................................................................................................ 258 Multiple Assignements ........................................................................................................................................................... 259

. 固定循环 .......................................................................................................................................... 260

.1 9.2 9.3 9.4 9.5 9.6 9.7 9.8 9.9 9.10

固定循环G8n ......................................................................................................................................................................... 260 G81- 钻孔循环 ......http://www.wendangwang.com/doc/efe960bed681037ac6d62544................................................................................................................................................................. 263 G82 -锪孔循环 ....................................................................................................................................................................... 264 G83- 深度钻孔循环 .............................................................................................................................................................. 265 DRP – G83 下一啄钻循环开始的准备距离 .................................................................................................................. 267 G84 – 无编码器的攻丝循环 .............................................................................................................................................. 268 G84 –带编码器的攻丝循环 .....................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544.......................................... 271 TRP(RMS) – Tapping Return Percentage ......................................................................................................................... 272 G85 – 绞孔循环 ..................................................................................................................................................................... 272 G86 -镗孔循环 ................................................................................................................................................................... 273

.11 G89 –带鍃孔的镗孔循环 .................................................................................................................................................... 273

. 11.

.1

.............................................................................................................................. 278

测量循环 ..........http://www.wendangwang.com/doc/efe960bed681037ac6d62544............................................................................................................................ 279

电子探头 .................................................................................................................................................................................. 279 DPP (DPT) – 定义测量循环参数 ................................................................................................................................. 281 G72 - 点的探测 ................................................................................................................................................................. 283 G73 – 孔探测循环 ................................................................................................................................................................. 284 G74 -刀具规格循环 ...................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544........................................................... 285 UPA (RTA) - Update Probe Abscissa ................................................................................................................................ 286 UPO (RTO) - Update Probe Ordinate ............................................................................................................................. 286 ERR - Managing Probing Errors ........................................................................................................................................... 286 OPERATIONS THAT USE A FIXED PROBE ................................................................................................................. 292

.2 11.3 11.4 11.5 11.6 11.7 11.8 11.9

.

.1 12.2

屏幕管理 ...................................................................................................................................... 29http://www.wendangwang.com/doc/efe960bed681037ac6d625443

视图查看 .................................................................................................................................................................................. 293 UGS (UCG) – 采用显示范围 (配合Machine plot使用) ............................................................................................ 293 UGS (UCG) -三维图像显示范围 ................................................................................................................................. 295 CGS (CLG) -清除显示范围 ................................................................................................................................................ 295 DGS (DCG) – 取消显示范围 ........................................................................................................................................ 295 DIS – 显示一个变量值 ......................................................................................................................http://www.wendangwang.com/doc/efe960bed681037ac6d62544................................... 296

.3 12.4 12.5 12.6

.

.1

修改程序的执行顺序 ................................................................................................................... 297

总括............................................................................................................................................................................................ 297

. 15. 16. 17. 18. 19.

.1

SPEED MACHINING ....................................................................................................... 322 MULTIPROCESS MNAGEMENET COMMANDS .................................................................... 322 HIGH LEVEL GEOMETRIC PROGRAMMING (GTL) .............................................................. 322 WORKING CYCLES FOR TURNING SYSTEMS ....................................................................... 322 FILTERS ......http://www.wendangwang.com/doc/efe960bed681037ac6d62544................................................................................................................................. 322 APPENDIX A: 字符和命令 .......................................................................................................... 323

字符表 ....................................................................................................................................................................................... 323

. 21.

B ............................................................................................................................... 325 APPENSIX C ................................................................................................................................ 325

Electro S.p.A.

of manual

K

. 前言

尊敬的阁下：

欢迎您使用Prima Electro公司的OSAI品牌产品，鉴于初次进行中文手册的编写，因时间仓促，编写过程中难免有纰漏，在此谨http://www.wendangwang.com/doc/efe960bed681037ac6d62544提醒您在参考本手册使用机器的过程中务必谨慎，有任何疑问或者可能有损害机器的情况下联系OSAI公司的技术服务人员。

本手册描写了用10系列CNC系统编写加工程序的步骤。其为程序员提供了在创建机器控制程序时需要的信息。

为了阁下能方便理解本手册内容，请首先阅读以下关于本手册阐释的习惯表达方式：

指令

在这些章节里论述的指令描述了一个特定的任务。在这些指令描述中采用了一个共用的结构。对于每个指令，以下信息将被提供：

[此处图片未下载成功]

指令名称

[此处图片未下载成功]

指令运算符

[此处图片未下载成功]

指令语法

[此处图片未下载成功]

操作数

[此处图片未下载成功]

规格参数表和注释

[此处图片未下载成功]

示例

如有可能，这些示例都包含了一部分程序和图标来说明这些指令在那一部分是如何工作的。

语法规定

[此处图片未下载成功]

关键词用粗体书写，他们不能省略，在实际应用中一定要输入。

操作数必须和相应的指令运算符配合才得以完整。指令运算符用粗体字显示，数值用斜体字显示，在被说明的过程中数值将以助记符代替，例如value，它是一个可以选择的数值，正式使用时候用恰当的数值代替它。首位的0可以被省略。例如：你可以编程G00为G，G01为G1。

示例：

(SCF,[value]) (SCF,[value])

，逗号和指令运算符SCF是关键字所以是粗体，必须按之前所说明的书写。value 是一个数值助记符，必须用一个合适的值代替。如前面所述，括弧表示value是一个可选择输入的值，如果不输入也无语法错误。   警告

为了正确的使用，遵循手册给出的某些信息很重要。对以下的标志要特别注意：WARNING, CAUTION 或 IMPORTANhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544T, 分别表示以下几类信息：

警告! 危险电压:它提示可能存在伤害人身或者设备的电压存在。 该标志的旁边会有关于如何避免这一个危险的文字说明。

警告! 综合危险: 它提示可能存在伤害人身或者设备的非电气因素。

该标志的旁边会有关于如何避免这一个危险的文字说明。

注意:突显主要的内容或者深一步阐释该话题。

专门术语

有些出现在手册中的术语解释如下：

控制器 指10系列数字控制单元，包含了前控制板单元和基础单元。

前操作面板 是机器和操作者之间的界面单元；有一个输出信息的监视器和输入数据的键盘。该控制板与基础单元相连。

基础单元 是硬件-软件单元，处理所有的机器功能。

[此处图片未下载成功]

[此处图片未下载成功]

. 10系列系统编程

系列加工程序是用由国际标准化组织的标准定义的一种特定语言编写。本章描述了该语言的成分并探讨了编程技术和规则。

.1 程序文件

系列加工程序存储在由10系列或者DOS名字命名的文件中。

[此处图片未下载成功]

系列名字最多48个字符的长度；这些名字用来识别加工程序文件夹中的各个程序。程序文件夹路径在机器安装时已经被设定（ 你也可以在AMP菜单中的human interface---PPDIR config修改）。

[此处图片未下载成功]

DOS名字最多8个字符的长度；这些名字用来识别常驻在DOS类型文件夹中的程序。

[此处图片未下载成功]

下编辑加工程序时，最后一行必须加上回车符，否则在程序执行过程中可能产生错误。  注释：

加工程序也可以在远程装置上存储，事先通过三字母命令GDV定义 （见第十二章）。

://www.wendangwang.com/doc/efe960bed681037ac6d62544r2.2 程序组成

[此处图片未下载成功]

字母命令代码

一个字母命令代码是一个能指示特点操作类型的字母。例如：G, X, Y, F 都代表一个字母命令代码。

[此处图片未下载成功]

字句

一个字句是一个由数值跟随在字母命令代码后组成。例如，以下这些都是字句： G1   X50.5   Z-3.15   F200   T1.1

[此处图片未下载成功]

程序段

一个程序的程序段包含了一套能识别一个将要进行的操作或者一系列将要进行的操作的口令。一个程序段最长包含126个字符。

一个加工程序其实就是一组程序段序列，其描述了一个具体的加工操作过程。  程序段

程序段可能包括几个部分。

当多个部分同时出现，必须按下表中所示的顺序出现： 程序删除  程序段注释

程序段注释可以在现有的程序段的任何位置插入。在 ；后面的任意字符都视为注释。

标签 标签符号

序号 数字序号

同步/异步 字符或者代码 所有允许语句或字符

[此处图片未下载成功]

delete程序段删除

程序段中的程序删除符提供了允许操作员是否执行以&quot;/&quot;字符开头的程序段的功能。 例如：

/N100 G00 X100

上面示例中显示的程序段可以被启用或者禁用，通过程序设定的软按键来实现，或者通过输入DSB来实现。

[此处图片未下载成功]

标签符号

标签符号允许编程员分配一个象征性的名字给程序段。一个标签可以包含至多6个文字数字的字符，这些字符必须在引号内。如果发生在具有程序删除符/的程序段，此标签必须在斜线后插入。 例如： &quot;START&quot; /&quot;END&quot;

当一个标签符号被用于一个跳转命令http://www.wendangwang.com/doc/efe960bed681037ac6d62544’GTO’ 中，则会跳转到该标签所代表的程序段。

[此处图片未下载成功]

数字序号

顺序数字字段是可选的。其允许程序员给每个程序段标号。一个顺序数字以字母N开头，可以至多有6个数字跟随(N0-N999999).

顺序数字必须出现在第一个操作数的前面及标签的后面。 例如： N125  X0

&quot;START&quot; N125  X0 &quot;END&quot; N125  X0

[此处图片未下载成功]

同步/不同步

字符&amp; 和 # 用于覆盖同步执行/不同步执行方式。关于同步的更多信息，请见“同步和程序执行”。 例如：

#(GTO,START, @PL1=1)

程序段类型

四种程序段可以用于加工程序：

[此处图片未下载成功]

程序段注释

[此处图片未下载成功]

运动程序段

[此处图片未下载成功]

赋值程序段

[此处图片未下载成功]

三字母命令程序段

[此处图片未下载成功]

程序段注释

一个程序段注释允许程序员在程序中插入随意的语句。这些语句可以是描述将要执行的程序的功能或者提供使该程序更易理解和注释的其它信息。

一个程序段注释不会为执行过程产生影响。控制器会在执行程序的时候忽视程序段注释。

一个程序段注释的第一个字符必须是一个分号(;). 该程序段注释的其它成分是一连串文字数字字符。例如： 一个注释不仅能在一个程序段插入，同样可在其它类型程序段的字符&quot;;&quot;后插入。所有位于一个分号；后面的字符视为注释。

[此处图片未下载成功]

例如：

X100 Y50 ; Motion block E1=10 ; Local variabhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544le E

(ROT,45) ; Rotation command

[此处图片未下载成功]

运动程序段

运动程序段遵照国际标准化组织和ASCII码的标准进行程序段编程。在一个运动程序段中没有特定的顺序来编写运动程序段的成分。 例如：

X500 Y20 F200

[此处图片未下载成功]

赋值程序段

赋值程序段用于直接从程序中书写变量的值。下表中展示了几种可能的赋值类型：

赋值类型 简单赋值 多重赋值

示例 E1=10, 15.5, 123.467

在多重赋值中，值的赋值如下： 10

数值传递到变量 E1 数值传递到变量E2

.5

数学算式赋值 系统变量赋值  三字母命令程序段

三字母命令程序段遵循RS-447标准用一个三字母的指示定义一个操作。例如： (ROT,45)

(DIS,&quot;message text&quot;)

为了10系列和系列8600之间的兼容性，有些命令可能用以下任一三个字母的代码编程。 UGS UCG； CGS CLG； DGS DCG； RQT RQU； DPA DSA； PAE ASC； PAD DSC； DPP DPT； IPB

； ROT URT； SOL DLO； UTO UOT； TOU TOF；

.467 数值传递到变量E3 E20=(E10 125*SQR(E23)) SN=1.5

[此处图片未下载成功]

轴坐标

轴坐标可以用字母ABCUVWXYZPQD来命名（根据AMP中的配置设定）并可用以下的范围来编程：

[此处图片未下载成功]

注意：

在 0.00001范围内不可能给坐标编程，因为0.00001是控制器接受的最小值。

坐标

在一个圆形http://www.wendangwang.com/doc/efe960bed681037ac6d62544的插补（G02 G03）中，R代表该圆的半径。

在一个标准的固定循环（G81-G89）中，R坐标规定开始的位置的值和返回后的值。该字母在以下范围内可以编程：

[此处图片未下载成功]

[此处图片未下载成功]

注意：

在 0.00001范围内不可能给坐标编程，因为0.00001是控制器接受的最小值。 在一个车螺纹程序段（G33）中，R坐标代表为多起点的相对0角位置的补偿值。

J 坐标

在圆形插补（G02-G03）中，I和J指定了一个弧形的中心的坐标。I指定横坐标（一般指X），J指定纵坐标（一般指Y）。I和J总是指定中心的坐标，该字母在以下范围内可以编程：

[此处图片未下载成功]

注意：

在 0.00001范围内不可能给坐标编程，因为0.00001是控制器接受的最小值。 I和J坐标同样用于深孔打钻循环（G83）。

在一个车螺纹程序段（G33）中，I的地址规定螺纹间距的等差变化值。 I  I-

和t

毫米/英寸

增加间隔

[此处图片未下载成功]

减少间隔

毫米/英寸 毫米/英寸

[此处图片未下载成功]

毫米/英寸

毫米/英寸

[此处图片未下载成功]

毫米/英寸

毫米/英寸

字母规定轴进给速率。该字母在以下范围内可以编程：

在G94中，F/分钟（G70）。

“t”值可以在一个程序段中编程来指定在程序段中完成一个移动的时间- 以秒为单位。在这种情况下程序段进给速率是：

distance

F =    * 60

“t”值只是在其所在的程序段中才生效。

[此处图片未下载成功]

://www.wendangwang.com/doc/efe960bed681037ac6d62544par

在G93中，F字母规定完成移动所需时间的倒数- 以分钟为单位，表达如下：

=  total distance   = 1/t (minutes)

当G93激活后，F字母在该程序段中是必须的，并且只影响该程序段。

在G95中，F指定轴进给速率- 毫米/主轴公转（G71）或者英寸/主轴公转（G70）.

[此处图片未下载成功]

[此处图片未下载成功]

a字母，在G71中表示 毫米/秒&#178;，在G70中表示

[此处图片未下载成功]

英寸/秒&#178;。该字母只有在其所编程的程序段才起作用，并且受限于其所在加工轮廓的该处的允许最大加速度。

字母

地址可以激活多种机器操作。编程范围从0到999。关于此字母的更多信息，请看第六章。

[此处图片未下载成功]

在G97中，S字母规定主轴转动速度，用公转/分钟表达。

在

[此处图片未下载成功]

G96中，S字母规定切割线速度，用米/分钟（G71）表达，或者英尺/分钟（G70）表达。以保持切割速度在切割表面上保持不变。

关于S字母编程的更多信息，请看第五章。

字母

字母规定加工所需的刀具和刀具补偿。在0.0至999999999999.300范围内可以编程。小数点左边的12个数字代表刀号，小数点右边的三个数字代表刀具补偿号。 第三章提供了关于T字母的详细描述。  S字母

/fpm

字母指定主轴的转动速度。在以下范围内可以编程： a 字母

[此处图片未下载成功]

mm/sec2  or inches/sec2

字母规定用于加工程序的加速度。其可以在以下范围内编程：

M, S 和T字母的具体特征根据他们在AMP中的设置而http://www.wendangwang.com/doc/efe960bed681037ac6d62544定。

在软件版本3.1中，系统在连续的运动（G27-G28）中执行这些字母是可能的。 但当进行实际应用的时候，制造商必须：

在AMP中设置所要的字母为&quot;ALLOWED IN CONTINUOUS&quot;。 编写逻辑来处理一个这样的字母。

在连续运动的模式下，一个设置了 &quot;ALLOWED IN CONTINUOUS&quot; 的字母将在被编程了的程序中执行。为了不锁定程序，该字母将会在&quot;否 WAIT&quot;模式下被执行。  在点到点的运动模式下，一个设置为 &quot;ALLOWED IN CONTINUOUS&quot; 的字母将在标准模式下执行。

相应地，编程员必须牢记这些字母产生怎样的效果取决于他们怎么是如何配置的：

字母

字母允许在连续运动和点到点的运动中改变补偿值。

在一个程序段中，h字母必须单独自己编程。它的值可能从0到300，并且可能要么是个整数或者是个E变量。

字母

字母为加工编程加工预备字母。以下部分论述该字母。  G字母

该部分展示在程序段中如何编写G字母。一个G字母命令代码是由G字母后面跟着一到两个数字(G00-G99)。目前，在100个可能的G字母中只有一部分是可用的。

子程序型G字母可以用一个三个数字的G字母来命名。此类G字母在第九章有描述。三个数字的G字母分类如下:

- G299 保留的

- G699 非模态子程序G字母 G700 - G998 模态G字母 G999 复位模态G字母

在程序段中，G字母必须位于序号数字后（如果用了序号）和操作数之前。例如： N100 G01 X0 – 操作数

在同一程序段，可以对几个G字母进行编程，只要它们相互之间兼容。下面的表格规定了G字母之间的兼容性，0表示G字母之间兼容，且可以在同一程序段内编程。1表示G字母之间不兼容，不可能在同一程序段编程以免出现错误。

[此处图片未下载成功]://www.wendangwang.com/doc/efe960bed681037ac6d62544

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

G字母兼容性

89 73 94 97 42 28 91 71 17 99 61

95 18 98

1 1 1 0 0 1 1 1 1 1 1 0 0 0 1 0 0 0 1 1 0 0 1 1 1 0 1 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0

1 1 0 0 1 1 1 1 1 1 0 0 0 1 0 0 0 1 1 0 0 1 1 1 0 1 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0

1 1 0 0 1 1 1 1 1 1 0 0 0 1 0 0 0 1 1 0 0 1 1 1 0 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

1 1 1 0 1 1 1 1 1 1 0 0 0 1 1 1 1 1 1 0 0 1 1 1 0 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

1 1 0 0 1 1 1 1 1 1 0 0 0 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1

0 0 0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 1 1 0 0 1 1 1 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 0 0

0 0 0 0 1 1 1 http://www.wendangwang.com/doc/efe960bed681037ac6d625441 1 1 0 0 0 0 0 0 0 1 1 0 0 1 1 1 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 1 1

0 0 0 0 1 1 1 1 1 0 0 0 0 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

0 0 0 0 1 1 1 1 0 0 0 0 0 1 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

0 0 1 0 1 1 1 1 0 0 1 1 1 0 0 0 0 1 1 0 0 1 1 1 0 0 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

0 0 0 0 1 1 1 1 0 0 1 1 1 0 0 0 0 1 1 0 0 1 1 1 0 0 1 1 1 1 1 1 1 0 0 1 0 0 0 0 0

0 0 1 1 1 1 1 1 0 0 1 1 0 0 0 0 0 1 1 0 0 1 1 1 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0

0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 1 1 0 0 1 1 1 0 0 1 0 0 0 0 0 0 0 0 1 0 0 0 0 0

0 0 0 0 1 1 1 1 0 0 0 0 0 0 0 0 0 1 1 0 0 1 1 1 1 0 0 0 0 0 0 0 0 1 1 1 0 0 0 0 0

0 0 0 0 1 1 1 1 1 1 0 0 0 0 1 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0 0

0 0 0 0 1 1 1 1 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1http://www.wendangwang.com/doc/efe960bed681037ac6d62544 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1

1 1 0 0 1 1 1 1 1 1 0 0 0 1 0 1 1 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1

1 1 0 0 1 1 1 1 1 1 0 0 0 1 0 0 0 1 1 0 0 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 1 1 1 1 1

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1

G02 G03 G04 G09 G16 G17 G18 G19 G20 G21 G27 G28 G29 G33 G40 G41 G42 G60 G61 G70 G71 G72 G73 G74 G79 G80 G81 G82 G83 G84 G85 G86 G89 G90 G91 G92 G93 G94 G95 G96 G97

G98 G99  注意：

1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1

下表给出了适用于控制器的G字母的总结。此默认的配置可以通过AMP进行修改。

代码总结 代号  G01 G02 G03 G33 G17 G18 G19  G28  G29 G98 G41 G42 G20 G21 G60 G61 G62 G63 G66 G67

类别  a a a a b b b  c  c d e e

模态  是 是 是 是 是 是 是 是 是 是  是  是 否 否 是 是 是 是 是 是 是 是 否 否 否 否

://www.wendangwang.com/doc/efe960bed681037ac6d62544r

描述

上电初始值 铣床  是 否 否 否 否 否 是 否 否 是  否  否 否 否 是 是 否

轮

廓

路

线

否  否 否 否 否 否 否

磨床 是 否 否 否 否 否 否 是 否 是  否  否 否 否 是 是 否 否  否 否 否 否 否 否

快速移动 直线插补 顺时针插补 逆时针插补

固定或者变化的螺纹加工

在一个预先定义的平面上进行圆弧插补和直径补偿

在第一轴和第二轴组成的平面上进行圆弧插补和直径补偿

在第一轴和第三轴组成的平面上进行圆弧插补和直径补偿

在第三轴和第二轴组成的平面上进行圆弧插补和直径补偿

连续移动并且在拐弯处带自动减速

连续运动并且在拐弯处不带任何减速

点到点的移动

工件原点预设（不关联镜像轴） 工件原点预设（关联镜像轴） 删除 G92 直径补偿功能关闭 左侧直径补偿 右侧直径补偿 开

启

关闭GTL轮廓路线 关闭 HSM 轮廓路线

开启 HSM 轮廓路线

the HSM profile in two with continuity

the HSM profile in tw with link Splits the HSM profile in two with edge

the HSM profile in two with reduced speed on edge

代号  G71 G81 G82 G83 G84 G85 G86 G89 G91  G09 G72  G73  G74

类别  f g g g g g g g h  j k  k  k

模态  是 是 是 是 是 是 是 是 是 是 是 是 否  否 否 否  否  否

描述

://www.wendangwang.com/doc/efe960bed681037ac6d62544r上电时初始状态 铣床  否 是 是 否 否 否 否 否 否 否 是 否 否  否 否 否  否  否

磨床 否 是 是 否 否 否 否 否 否 否 是 否 否  否 否 否  否  否

以英寸为单位编程 以毫米为单位编程 取消固定循环 钻循环 鍃孔循环 深孔钻孔循环 攻丝循环 铰刀循环 镗孔循环

带延时的镗孔循环 绝对值编程 增量值编程 采用绝对坐标系

程序段结尾处延时 程序段结尾处减速

probing with probe tip radius compensation

probing with probe tip

compensation

for theoretical deviation from a point without probe tip radius compensation

time (V/D) feedrate programming mode

用毫米/分钟或者英寸/分钟给进给率编程

programming in ipr or mmpr

固定表面切割即线速度 (英寸/分钟  或者米/分钟)

用转/分钟为单位对主轴转速编程

G94 G95  G97

l l  m

是  是 是 是  是

否  是 否 否  是

否  否 是 是  否

同步和程序执行

术语“同步的”和“不同步的”只适用于不包含运动的加工程序段，即赋值程序段或者算式程序段。一个运动程序段是指任何包含了轴运动和其他运动的程序段。

[此处图片未下载成功]

轴移动

[此处图片未下载成功]

M代码

[此处图片未下载成功]

S代码

[此处图片未下载成功]

T代码http://www.wendangwang.com/doc/efe960bed681037ac6d62544

一个同步程序段只有在该程序中位于其之前的运动程序段完成后才被考虑和执行。

另一方面，不同步程序段在被加工程序的译码器解读后就会马上执行，即使此前的移动运动仍在进行中。 不同步程序段执行的优点在于变量赋值和复杂的计算可以在移动之间进行。这样可以减少因计算耗时引起的两个运动程序段的等待时间。

默认同步

通电时，以下的命令和字母是自动调用同步的：

[此处图片未下载成功]

[此处图片未下载成功]

UDA, SCF, RQO, IPB, DLY, WOS, WAI, SND, GTA, REL, UPR, TCP, UVP, UVC  G16, G17, G18, G19, G72, G73, G74 其它所有的命令不是自动调用同步的。

此默认值可以被更改。这就是说在通电时默认为同步的指令可以变成不同步，在通电时默认为不同步的指令可以变成同步。下面的部分会解释怎么重定义默认的同步。  注意：

对于GTA, UPR, TCP, UVP, 和 UVC指令，默认同步不能修改。

重定义同步

在一定环境下，加工程序可能要求修改默认同步。

如果命令是默认同步的，想让程序译码器解读该命令时立即执行（不同步操作），“&amp;”可以编程于此程序段的首位，紧接“n”数字后。

如果命令是不同步的，且你想激活同步操作，那么此程序段的第一个字符必须是#。 #和&amp;只在其编程的程序段中起作用。

为了避免对工作部件可能的损坏，注意考虑到同步的时候因为相邻的运动程序块过渡时因重新加载程序指令缓冲器和重新开始计算时所引起的停顿。

加工程序译码器

当系统解读一个加工程序段，系统会执行各种活动，这取决于程序段的类型：

[此处图片未下载成功]

一个运动程序段将会被加载在运动缓冲器队列。缓冲器容量大小可以通过AMP从2到128个程序段配置。

[此处图片未下载成功]://www.wendangwang.com/doc/efe960bed681037ac6d62544r

一个不同步的赋值或者计算程序段会被执行。

三种原因会引起加工程序译码器停止解读程序段：

[此处图片未下载成功]

运动缓冲器满了。待当前运动程序段完成后，译码器将会读取另一个运动程序段并将其加载到运动缓冲器行列。

[此处图片未下载成功]

一个包含了一个同步命令或者强制同步的代码的非运动程序段被解读。直到上次加载的运动程序段执行完毕，译码器才会再次启动。

[此处图片未下载成功]

产生错误时。

执行顺序

.  直径轴  2.  3.  4.  5.  6.  7.  8.

长实数型数值编程限制说明： 以下是对长实数型数值的限制

[此处图片未下载成功]

数值最多包含15个数位

[此处图片未下载成功]

最多12个整数位

[此处图片未下载成功]

最多9个小数位

如果编程的数值超过了12个整数位，系统会显示错误信息。

如果多于9个小数位，则系统不显示任何错误，但是会忽略第9个小数位后面的数字。

[此处图片未下载成功]

坐标比例变换 (SCF)  单位转换 (G70 G71)  坐标空间虚拟转换 ( u v w )  绝对/增量型编程 (G90 G91)  镜像加工 (MIR)  平面旋转(ROT)

工件原点 (UAO UTO UIO G92)

3. 轴编程

.1 轴运动编码 3.1.1

定义轴运动

在本手册中，轴运动方向依照EIA标准RS-267定义。通常，我们总是认为刀具是向部件移动的，不管在实际过程中是刀具向部件移动或者部件向刀具移动。 基本的移动可以用下表列出的G字母定义：  G代码 G01 G02 G03 G33

功能 快速轴定位 直线插补 顺时针圆弧http://www.wendangwang.com/doc/efe960bed681037ac6d62544插补 逆时针圆弧插补

固定螺距或变化螺距螺纹线加工

.2 G00 –快速轴定位

定义快速进给率下的线性运动，对于程序段中所有编程的轴是同时且相互协调的。  语法

[G-codes] [axes] [offset ] [F..]  [auxiliary]   其中：

-codes 是其他与G00兼容的G字母（见第一章“兼容的G字母”表）。

轴名称，其后跟随一个数值。该数值可以是一个十进制的值或者是一个E变量。在一个程序段中高达九个轴可以被编写。

轮廓上的补偿因数。对于X,Y,Z轴来说，这些因数分别用u,v,和w键入。更多信息请见第四章“变轴补偿”

进给率。F地址后面跟随着进给率值。该参数不影响G00的速度，而是保留对随后的运动产生影响，快速进给率在AMP中被定义。

用来编写加速度。

可编程诸如M,S,T等辅助字母。在一个程序段中可以编程高达4个M字母，1个S

（主轴速度）和1个T（刀具选择）。

3.3 G01 – 直线插补

定义加工进给率下的直线移动，对于程序段中所有编程的轴是同时和插补的。  语法

[G-codes] [axes] [offset ] [F..]  [auxiliary]

其中： G-codes

其他与G01兼容的G字母（见第一章“兼容的G编码”表）。

轴名称，其后跟随一个数值。该数值可以是一个十进制的值或者是一个E变量。在一个程序段中高达九个轴可以被编写。  offset

轮廓上的补偿因数。对于X,Y,Z轴来说，这些因数分别用u, v, 和 w键入。更多信息请见第四

章“变轴补偿”。

用于移动的进给率。其同F字母一起给出且跟随进给率值。如果被省略，系统会使用之前编程的进给率。如果没有编程进给率，控制器http://www.wendangwang.com/doc/efe960bed681037ac6d62544会报错。

用来编写加速度。

可编程的M, S和 T辅助字母。在一个程序段中可以编程高达4个M字母，1个S （主轴速

度）和1个T（刀具选择）。  示例：

这个示例表明如何编程一个G01编码。

[此处图片未下载成功]

程序：

(UGS,X,-10,100,Y,-10,50) N70 G0 X10 Y10

G01 X90 Y40 F200

3.4 G02 G03 – 圆弧插补

这些代码定义了下面的圆弧运动。

[此处图片未下载成功]

G03

顺时针圆弧插补

[此处图片未下载成功]

(CW) 逆时针圆弧插补(CCW)

这些圆弧移动在加工进给率下进行，同程序段中所有被编程的轴是同时且插补的。  语法

[G-codes] [axes] I.. J.. [F..]  [auxiliary]  或

[G-codes] [axes] R.. [F..]  [auxiliary]   G03 [G-codes] [axes] I.. J.. [F..]  [auxiliary]  或

[G-codes] [axes] R.. [F..]  [auxiliary]    其中： G-codes

其他与G02和G03兼容的G字母（见第一章“兼容的G字母”表）。

轴名称，其后跟随一个数值，该数值可以直接用一个十进制的值或者用一个E变量。

如果在程序段中没有轴被编程，在当前激活的插补平面上轴移动是一个完整的圆弧。

圆心的横坐标。这个值以毫米为单位，可以直接编程或者用一个E变量间接编程。当相应的轴是直径轴时，横坐标表示的是直径单位。不管你使用的是何种插补平面，横坐标总是用I表示。

圆心的纵坐标。这个值以毫米http://www.wendangwang.com/doc/efe960bed681037ac6d62544为单位，可以直接编程或者用一个E变量间接编程。当相应的轴是直径轴时，纵坐标表示的是直径单位。不管你使用的是何种插补平面，横坐标总是用J表示。 注意：参数R不能用于360度的弧形。

圆弧半径，可代替I和J坐标。如果圆周的弧度小于或等于180度，编程时半径必须带正号；如果圆周的弧度大于180度，编程时半径必须带负号。 注意：R不能用于360度的弧形。

用于移动的进给率。其同F地址一起给出且跟随进给率值。如果被省略，系统会使用之前编程的进给率。如果没有编程进给率，会出现错误。

用来编写加速度。 auxiliary

可编程的M, S和 T辅助字母。在一个程序段中可以编程高达4个M字母，1个S （主轴速

度）和1个T（刀具选择）。

说明：

可编程的最大弧形为360度，即一个整圆。在编程一个圆弧插补程序段时，插补平面必须用G16, G17, G18, G19定义。在接通电源后，G17自动被激活。

圆弧的起点是上一个运动程序块的终点，对于I,J圆弧编程，起始点和终点两者的半径差值要比允许值(0.01 mm or 0.00039 英寸)要小。如果这个差值等于或大于允许值，控制器会显示一个错误信息，且不会执行圆弧动作。

增量编程(G91)可与圆弧插补一起使用。用G91，终点和圆弧运动的中心将参考之前程序段中编程的位置。 圆弧插补的方向（顺时针或逆时针）通过查看轴的正方向来定义。下面这个示例展示了当前插补平面上圆弧插补的方向。

[此处图片未下载成功]

Z

圆弧插补的方向

圆弧插补，用圆弧中心I和J坐标绝对编程。 N14 X10 Y20

G2 X46 Y20 I28 J20 F200 N16 G3 X64 Y38 I46 J38

[此处图片未下载成功]

圆弧插补，用圆弧半径的R值绝对编程。 N14 X10 Y20

G2http://www.wendangwang.com/doc/efe960bed681037ac6d62544 X46 Y20 R18 F200 N16 G3 X64 Y38 R18

圆弧插补，用坐标J和I增量编程。 N14 X10 Y20

G2 G91 X36 I18 J0 F200 N16 G3 X18 Y18 I0 J18

圆弧插补，用半径R值增量编程。 N14 X10 Y20

G2 G91 X36 R18 F200 N16 G3 X18 Y18 R18

.5 CET (PRC) – 圆弧起点终点半径差阀值

在圆弧插补中，CET 定义出圆弧起点和终点的半径差异容许值。  语法 CET=value   其中: value   特征:

如果起点和终点的半径差异小于容许值但不等于零，系统便会根据CET和ARM的设定值来调整这个圆弧。 但是当半径差异大于或者等于了CET设定的容许值，那么会产生错误信息且程序不被执行，这种情况下，要么修改程序或者增大CET的容许值。 CET 可以通过以下几种途径修改

[此处图片未下载成功]

:

在AMP里面设定。

[此处图片未下载成功]

在MDI手动指令输入框输入。

[此处图片未下载成功]

在加工程序里面添加一条赋值给CET的语句。

遇到了复位命令后会重新恢复到AMP所设定的CET的值。

示例: CET=0.02

定义 0.02 毫米为容许值

容许值，毫米为单位. 缺省值是 0.01 毫米.

.6 FCT – 整圆缝合临界值

在圆弧插补中，FCT定义了圆弧起点和终点之间的距离，如果圆弧起点和终点的距离小于这个值，则系统把终点视为与起点重合，然后从起点开始，按所编程的插补方向画一个整圆回到该起始点，这种情况常常发生在一个圆弧起点和终点极其接近的情形。

语法 FCT=value   其中: value

的值可以通过以下途径修改

://www.wendangwang.com/doc/efe960bed681037ac6d62544r[此处图片未下载成功]

:

遇到复位命令后会重新恢复到AMP所设定的FCT的值。

示例: G71

=0.005

这个示例中, FCT 定义了临界值是 0.005 毫米。

在AMP里面设定。

[此处图片未下载成功]

在MDI手动指令输入框输入。

[此处图片未下载成功]

在加工程序里面添加一条赋值给CET的语句。

毫米表示的值。缺省值是0.001 毫米。

.7 ARM – 圆弧修正模式

参数是用来修正一段圆弧（适用于以圆心坐标I，J和圆弧终点确定的圆弧），试想起点到圆心的距离（实则半径）与终点到圆心的距离（实则也是半径）不同，则该圆在数学几何上不可能成立，于是该参数会修正这种错误，使得该圆弧符合数学几何要求。

当一段圆弧的起点和终点半径存在差值且小于CET指定容许值时候，这段圆弧就会被修正。 在执行一段圆弧之前，系统会计算起点和终点的半径差值并执行以下操作：

[此处图片未下载成功]

如果差值等于0，那么系统理所当然地不做任何修正。

[此处图片未下载成功]

如果差值大于CET的容许值，则不会执行该程序段且产生错误信息。

[此处图片未下载成功]

如果差值存在且小于CET指定的容许值，那么控制器会执行ARM所设定的修正模式去修正该圆弧的参数然后描绘该圆弧。

[此处图片未下载成功]

如果起点终点距离小于FCT的值，则会被迫形成一个整圆。如果该程序段含有半径（直径）补偿，系统会进行两次检查，第一次是在不含补偿的加工路径情况下进行判断，另一次在考虑加入了补偿后的加工路径的情况下进行判断。

语法

=arc mode   其中: arc mode

1 2

是一个http://www.wendangwang.com/doc/efe960bed681037ac6d62544数字定义了修正的模式，以下是合法的数字代号 在CET容许范围内更改圆心（默认模式）。 更改起点。

更改圆心而不顾CET范围。

特征:

当圆心超出了CET容许范围的修正。

默认值是0

修正模式值可以通过以下途径修改

[此处图片未下载成功]

:

在AMP里面设置

[此处图片未下载成功]

在MDI手动指令输入框输入

[此处图片未下载成功]

通过在加工程序里面书写一个ARM赋值语句。 以下的示例阐明了各种模式的修正过程.

这是一段穿过起点和终点的圆弧且其新圆心在CET值的范围内新找一个点取代原来的圆心，新圆弧的半径则是取此前两半径的平均值。

[此处图片未下载成功]

point 起点，averaged radius 平均半径， final point 终点， C

[此处图片未下载成功]

编程圆心， CS新圆心

=1

point 起点，averaged radius 平均半径， final point 终点， C编程圆心， CS新圆心

这是一段其半径取两者平均值且新圆心不理会是否在CET范围内的圆弧。

[此处图片未下载成功]

point 起点，averaged radius 平均半径， final point 终点， C 编程圆心， CS 新圆心

=3

如果半径差值在CET范围内，圆弧会以起点终点的半径平均值确定新圆心：如果此圆心在CET范围内，则采纳该圆心并仍然穿过原来的起点和终点，且以他们到旧圆心的半径平均值为新的圆弧半径；如果新圆心与旧圆心的距离超出CET值的范围，则会仍保留原来的圆心，然后以原来的半径平均值作新的圆弧。

://www.wendangwang.com/doc/efe960bed681037ac6d62544ar= programmed center

[此处图片未下载成功]

CS = displaced center

[此处图片未下载成功]

poin t起点，averaged radius 平均半径， final point 终点， C 编程圆心， CS 新圆心

在ARM=1或者ARM=3的情况下圆弧起点和终点位置被系统修正，明显的产生了“位置跳跃”，可能

会与所期望的路径产生偏差。

=1的时候在起点位置产生的偏差幅度就是起点终点半径差值。 ARM=3的情况下位置跳跃均发生在起点和终点位置。

如果避免这些偏差产生伺服误差报警，则建议CET的设定值比伺服误差上限值小。

.8 3.9

–圆弧插补减速阀值                              CRK –圆弧插补减速常数

参数（圆弧插补减速阀值）和CRK（圆弧减速常数）是用在圆弧插补时进行减速，减速的方式取决于CRT的正负号。减速方式可以是：

-如果CRT &gt; 0，则仅减速率是一个与圆弧半径相关的函数。

-如果CRT = 0，则减速率是一个与圆弧半径和离心加速度相关的函数。 -如果CRT &lt; 0，则减速率是一个与半径和允许的位置跟随误差相关的函数。  语法

= value    其中:

是一个数值，如果该数值大于0，则如果圆弧半径小于该数值，那么会采用圆弧减速，如果是0，则取消该参数的作用；如果该数值小于0，则表示的是实际圆弧和所编程的圆弧差别不能超过该数值的绝对值，单位是毫米。

= value    其中:  value

&gt; 0 时

是一个定义减速率的常数，默认值是1。

是一个定义减速率的常数，减速方法参考离心加速度（V&#178http://www.wendangwang.com/doc/efe960bed681037ac6d62544;/R）。

该数值是位置环增益值（Kv），它需要和轴参数所设定的位置环增益数值一致。

= 0 时                 CRT &lt; 0 时

如果 CRT 和 CRK 都是0，则对圆弧插补不采用任何的减速方式。 说明：

的数值指定了采用了何种方式的圆弧插补减速，如果：

&gt; 0 =&gt;

把任何一个整数给CRT，则表示半径小于该数值的圆弧插补会采取减速，而CRK与其同时是给出了减速比率。下图给出了一个例子，在图中假定了速度Vp是1，而CRT的值也是1。

CRT = 0 =&gt;

如果CRT=0，而CRK不是0，那么在圆弧运动中，其实际加工速度则依据以下公式得出：

lav = 括号中两者较小值 （

,  V Prog ）

其中V lav是得出的实际加工速度，a是取圆弧插补的两个轴的加速度

在AMP设定中最小的一个，radius是圆弧的半径。       V Prog是加工程序中编写的进给率。

此时CRK是按照如下方式进行修正。  V lav =括号中两者较小值 （ CRK *

*radius,  V Prog ）

*radius再和V Prog

显然CRK是一个比例因子，可以调大或者调小进行比较。

&lt; 0 =&gt;

设置任何一个负数给CRT，圆弧加工时会减速，且CRT的数值的绝对值代表位置误差范围，即加工该圆弧时误差范围不能超过此数值。除此之外，还给出了加工圆弧时的最大速度，根据以下公式：

= CRK  * 2 * R * abs(CRT) * f(VFF,FLT_2) Vmax是最大允许速度，abs（CRT）是CRT的绝对值。

(VFF,FLT_2) 是关于速度前馈（VFF）和滤镜样式2的函数。关于滤镜，请参考本手册“滤镜”这一章节。 注意：://www.wendangwang.com/doc/efe960bed681037ac6d62544ar

由于圆弧速度受限于VFF的值，当启用了VFF后需要在驱动器和轴参数里设置相同的VFF百分比。

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

.10 螺旋状插补

和G03仅在一个程序段中编程单个螺旋状路径。但当系统通过在圆弧插补过程中的同时移动一个垂直该平面的轴线性移动则会形成螺纹状。

为了编程一个螺旋状路径，只要增加一个深度坐标和螺距(K)到圆弧插补程序段中指定的参数。  语法

[G-codes] [axes] I.. J.. K.. [F..] [auxiliary]  或

[G-codes] [axes] R.. K.. [F..] [auxiliary]   G03 [G-codes] [axes ] I.. J.. K.. [F..] [auxiliary]  或

[G-codes] [axes ] R.. K.. [F..] [auxiliary]   其中：

-codes                其他与G02和G03兼容的G字母（见第一章“兼容的G字母”表）。  axes

轴名称，其后跟随一个编程了的数值（十进位的值或者E参数）。

如果在程序段中没有轴被编程，在活动的插补平面上轴移动会生成一个完整的圆弧。

圆心的横坐标。这个值以毫米为单位，可以直接编程或者用一个E参数间接编程。当相应的轴是直径轴时，横坐标表示的是直径单位。不管你使用的是何种插补平面，横坐标总是用I表示。

圆心的纵坐标。这个值以毫米为单位，可以直接编程或者用一个E参数间接编程。当相应的轴是直径轴时，纵坐标表示的是直径单位。不管你使用的是何种插补平面，横坐标总是用J表示。  R  K

圆弧半径。其用R地址指定，其后跟随一个长度值，且可代替I和J坐标。

螺距。该参数用K地址指http://www.wendangwang.com/doc/efe960bed681037ac6d62544定，其后跟随螺距值。如果螺纹深度小于1个螺距，该螺距值可以省略。

进给率。由F地址指定，其后跟随一个值。如果该值被省略，系统将会使用之前编程了的进给率。如果没有进给率被编程，系统将会显示错误信号。

说明：

如果Z是K的倍数，那就没有必要编程最后一个点。

如果深度不是PITCHES的整数倍，即如果Z不是等于n*K, 圆周的长度必须用PITCH数的小数部分计算。例如，如果Z=2.7*K，那么必须编程的弧形是is 360 * (2.7 - 2) = 252度。

可编程的M, S和 T辅助字母。在一个程序段中可以编程高达4个M字母，1个S   （主轴速度）和1个T（刀具选择）。

G2 X . . Y. . Z . . I . . J . . K . . F. .

在这个示例中，X, Y, I, 和 J地址参考圆弧编程；Z和K地址参考螺旋编程，且分别是深度和螺距。下图显示了一个螺旋状插补的典型图例。

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

螺纹尺寸规格

.11 G33 – 等螺距或者变螺距螺纹加工

定义了圆柱体，锥形，球杆面螺纹加工运动，包括等螺距和变螺距加工，加工的运动速度与旋转轴转速同步，所设定的参数会指明了是那种螺纹加工方式。  语法

[axes] K.. [I..] [R..]

其中: axes   K  I

轴名称，后面跟随者数字。

螺距值 (必须指定). 对于变螺距, K 给出的是初始值。

变螺距的等差值，如果螺距是逐渐变宽，则为正数，如果螺距逐渐变窄，则是负数。

与旋转轴0&#176;的偏移值，这用于多头螺纹加工，也就是每条螺纹的开始位置的角度值，以区分各条螺纹的开始位置，避免它们重合。

所有这些数值可以用数字来http://www.wendangwang.com/doc/efe960bed681037ac6d62544直接编程或者通过E变量来编程。

在螺距等值递减加工中，开始螺距，螺距等差值，和螺纹加工总距离要满足以下关系，以确保最后一个螺距在到达螺纹终点时还是大于0，其数学关系如下：

&lt;  K&#178;/ 2(Zf - Zi)  其中: I  K

螺距等差值 开始螺距值

螺纹总距

在螺纹加工过程中“循环停止”和快速移动进给率的按钮功能会被忽略，且主轴速度快速移动选择键要通过PLC来禁用。

可以被通过相应的按钮或者VFF命令语句来禁止。

定值螺纹加工

下面图标阐明了定螺距螺纹加工方式，注意U轴是一个直径轴。

圆柱体螺纹加工

程序: G33 Z-100 K2

(Zf - Zi)

[此处图片未下载成功]

[此处图片未下载成功]

圆锥体螺纹加工

程序: G33 U40 Z-80 K3

圆柱体和圆锥体结合的螺纹加工

[此处图片未下载成功]

程序: G33 Z-95 K2 .5 Z-100 U52 K2.5

变螺距螺纹加工

下图阐明了变螺距螺纹加工方式，注意U

[此处图片未下载成功]

轴是一个直径轴。

圆柱体的增螺距螺纹加工

[此处图片未下载成功]

程序: G33 Z-50 K4 I1

圆锥体的增螺距的螺纹加工

程序: G33 U50 Z-40 K4 I1

减螺距的圆柱体螺纹加工

[此处图片未下载成功]

程序: G33 Z-50 K10 I-1

多头螺纹加工

在G33中一个R变量使http://www.wendangwang.com/doc/efe960bed681037ac6d62544得旋转轴的起点可以在不同的位置（起点角度），这个位置取决于R变量所定义的起点的角度值。

这样就可以将刀不动，只是移动旋转的轴到相应的角度来开始对应的那条螺纹的加工，就不需要像以前那样把到移动到相应的起点位置来开始加工。

示例:        三螺纹： N37 G33 Z3 K6   .  .  . N41 G33 Z3 K6 R120   .  .  .

G33 Z3 K6 R240

第一条螺纹起点

第二天螺纹起点

第三条螺纹起点

[此处图片未下载成功]

[此处图片未下载成功]

.12 旋转轴

在系统配置中，轴可以设置为旋转轴。

编程旋转轴运动，其与在同一程序段中编程的其他轴同时且插补：

[此处图片未下载成功]

总是使用十进制度（从 0.00001 到  99999.99999），从预先选定的原点开始。

[此处图片未下载成功]

在旋转移动中，速率总是用度/分表示(dpm,F5.5格式)。例如，用F75.5，轴以75.5度/分的速度移动

.13 循环轴

循环轴可以是旋转轴或线性轴，其位置被控制在0和一个正数之间，这个正值可以通过rollover pitch参数配置，运动过程中超过了这个正数极限便再次从0开始，常见的是旋转的时候从0&#176;到359&#176;时，再旋转多1&#176;时便再次是0&#176;而不是360&#176;

循环轴可以在一个程序段中被编程为两种不同的模式。

绝对模式(G90)         以度为单位编程移动。

增加模式(G91)         从现在的轴位置开始，以度为单位作为增量编程。

– 绝对模式 在这种模式中：

[此处图片未下载成功]

显示的位置从0到 3http://www.wendangwang.com/doc/efe960bed681037ac6d6254459.99999度

[此处图片未下载成功]

编程范围从0到 359.99999度

[此处图片未下载成功]

轴旋转方向取决于编程移动的符号。按照惯例，一个带正号的移动是顺时针的，带负号的移动是逆时针的。

例如,我们假设旋转轴B开始定位在90度位置然后接着编写并执行以下程序段。

B45

[此处图片未下载成功]

180

顺时针旋转

B轴实际过程中便顺时针旋转315度，从90度位置到达45度角的绝对位置（移动的符号为正） 再举下例，现在我们假设B旋转轴在90度位置，接下来编写并执行以下程序段： G90 B-0

[此处图片未下载成功]

90

逆时针旋转

轴逆时针旋转90度至绝对0度位置，因为移动的符号为负。

- 增量模式

当一个循环轴在增量(G91)模式中被编程，下列条件适用： 显示的位置从0到 359.99999度

编程范围从 /-0.00001到 /-99999.99999度

轴旋转方向取决于编程移动的符号。按照惯例，一个带正号的移动是顺时针的，带负号的移动是逆时针的。

[此处图片未下载成功]

当编程范围大于 359.999度时，显示的位置会与编程范围不一致。

例如，如果B旋转轴的绝对初始位置是0度，接下来编写并执行以下程序段：

B765

增量顺时针旋转

轴做了两个完全顺时针旋转加45度(360   360   45 = 765)。

.14 伪轴

伪轴是一个可以定义为看起来类似插补轴一样但仅受控于PLC的轴，它的名字可以是X,Y,Z,A,B,C,U,Vhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544,W,P,Q,D, 在加工程序中你可以定义3个伪轴，而在AMP你可以定义多达6个。实际的应用可以是控制一个气压输出，如果定义P是控制压力的伪轴，你可以在PLC编辑该功能使得执行加工程序时遇到P20会输出20bar的压力，P10.5会输出10.5bar的压力。

.15 Diameter Axes直径轴

铰刀/端面车削头能安装在主轴上且和其他轴同时受控，设置一个这样的轴（通常是U轴）可以实现如下：

[此处图片未下载成功]

钻圆筒形孔或者锥形孔

[此处图片未下载成功]

[此处图片未下载成功]

Circular radiuses (concave or convex)  倒角

[此处图片未下载成功]

加工凹槽

[此处图片未下载成功]

端面切削

[此处图片未下载成功]

车螺纹

跟设置其他直线轴一样，只是坐标是用直径来表达。

在执行一个带有直径轴的程序段，加工平面必须被指定，例如：

Z U  上例中，Z和U的顺序很严格，例如G16 UZ和G16 ZU定义的是完全不同的切削平面。

直径补偿（G41或者G42）和机械加工余量（MSA）可以应用于直径轴编程。

例如：

以下的范例是一个用在精加工的铰刀/端面切削操作。

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

(DIS, &quot;FINISHING WITH R/F HEAD&quot;) N117 F60 S630 T9 .9 M6 N118 G16 Z U   ;定义加工平面 N119 (UAO, 2)   ; N120 (UTO, 1, Z-200)  ; N121 X Y160 M3   ;移动到孔1 N122 G41http://www.wendangwang.com/doc/efe960bed681037ac6d62544 Z2 U51

G1 Z-1 U44 .98  ;倒角去边 N124 Z-44   ;直径45的孔 N125 G G40 U40  N126 Z2 F40 S380 N127 G41 Y U106   ;移动到孔2 N128 G1 Z-1 U99 .975  ;倒角去边 N129 Z-15   ;加工直径100的孔 N130 r5   ;半径为5 N131 U60   ;执行鍃孔 N132 r-3   ;半径为3 N133 Z-40 U40   ;斜面加工 N134 G40 Z-44   ; N135 G U35 N136 Z100 M5 N137 G16 X Y  N138 (UAO,1)

用G02/03或者r字母编程或者直径补偿（G41/G42）编程时，方向关系可以参考下图，因为负直径方向很少用到，所以一般你只需要考虑前面两个象限。

[此处图片未下载成功]

3.16 UDA - 双轴

将一个或多个轴作为另一个定义为主动轴的从属轴是可行的。在这种方法中，只有主动轴的运动需要被配置，因为从属轴同主动轴相关连，他的运动由主动轴决定。  语法

(UDA,master1/slave1[,master2/slave2,master3/slave3,master4/slave4]) (UDA)

其中：

. . . master4 是主动轴名字（每个轴有一个ASCII字符）。可以编程至多4个主动轴。 slave1. . . slave8 轴。

parameters  特征:

双轴不需要在AMP里面进行专门的设置。

在一个(UDA...) 命令以后，主动轴的运动极限受限于从属轴，其关系如下 t

没有参数的时候，也就是只有“(UDA)”，是取消双轴功能。

是从属轴的名字（每个轴有一个ASCII字符）。每个主动轴可以最多编程8个从属

正极限 = 取最小值  ( 主动轴正极限, 主动轴此时位置   从属轴此时位置 – 从属轴 http://www.wendangwang.com/doc/efe960bed681037ac6d62544正极限 )

如果是镜像运动，于是行程应该是与从属轴的负极限相关，所以便会是：

正极限 = 取最小值  ( 主动轴正极限, 主动轴此时位置   从属轴此时位置 – 从属轴 负极限 )

同理，关于负极限，其关系如下：

负极限 = 取最小值  ( 主动轴负极限, 主动轴此时位置   从属轴负极限 – 从属轴此时位置 )

如果是镜像运动，则将会是：

负极限 = 取最小值  ( 主动轴负极限, 主动轴此时位置 -从属轴正极限  从属轴此时位置 )

当(UDA...)命令被执行时，必须对主动轴和从属轴进行归零。 RESET命令不会取消主动轴和从属轴之间的联系。

(UVP, UVC). 双轴可被用于旋转平面或两极或圆柱形坐标(UVP, UVC)。 双轴，不管是主动轴还是从属轴，必须在真实的轴上而不是虚拟轴上定义。  注意：

主动轴和从属轴名字必须用斜线/分隔。   如果要使从属轴是主动轴的镜像运动，那么要在从属轴前面加“-”，但是不能在主动轴前

面加这个符号。

示例： (UDA,X/-U)

是从属的，且是X的镜像运动

, C, D从属于A的运动，C是A的镜像运动

(UDA, A/B - CD)

(UDA, X/AB/-14)        A， B 是X轴的从动轴而第14轴是X轴的镜像。

.17 SDA – Special Dual Axes

将一个或多个轴作为另一个定义为主动轴的从属轴是可行的。在这种方法中，只有主动轴的运动需要被配置，因为从属轴同主动轴相关连，他的运动由主动轴决定。主动轴和从属轴的运动关联动作即使在未归零的情况下也能发生。   语法

(SDA,master1/slave1[,master2/slave2,master3/slave3,master4/slave4]) (SDA)

://www.wendangwang.com/doc/efe960bed681037ac6d62544ar其中：

. . . master4 是主动轴名字（每个轴有一个ASCII字符）。可以编程至多4个主动轴。

. . . slave8

是从属轴的名字（每个轴有一个ASCII字符）。

programmed by ID can refer to axes not belonging to the active process, therefore they can be logical axes or axes belonging to other processes, but shared with the logics.You can program up to 8 slave axes per master, 6 of which do not belong to the process.

parameters (SDA) without parameters disables the special dual axes mode (SDA) 说明：

an (SDA...) command, the positive operating limit is the minimum between the positive limit of the master axis and the current position of the master plus the distance that may be covered by the slave axis. In short:

= min(Master PositiveLim, MasterPosition   Slave PositiveLim - SlavePosition)

the case of a &quot;mirror&quot;, the distance that may be covered by the slave refers to its negative limit, so it http://www.wendangwang.com/doc/efe960bed681037ac6d62544will be:

= min(Master PositiveLim, MasterPosition - Slave NegativeLim   SlavePosition) The considerations made for the positive limit also apply to the negative limit:

= max(Master NegativeLim, MasterPosition   Slave NegativeLim - SlavePosition)

the case of a mirror, it will be:

= max(Master NegativeLim, MasterPosition - Slave PositiveLim   SlavePosition) Upon activating the (SDA,...) command the master and the slaves need not be referenced.

(UDA,...) programming resets all previous UDA or SDA, updating the last Master/Slave association programmed.

RESET command does not remove the master/slave association.

allows one to perform the zero point micro-search cycle with dual movement active.  In this case performing the zero point micro-search cycle, the system simultaneously moves the associated slaves.  At the end of the search the mastehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544r axis is referenced where as the slave axes are not.  In order to reference the slave axes they should be exchanged, one by one, with the master axis by new SDA programming and the zero point micro-search cycle repeated for each one of them, redefined as the master.  The initialisation of the slaves is not however necessary if one intends to program only the master with SDA active.

use of the SDA function is recommended in cases where a zero point micro-search cycle is to be

performed following a shutdown of the system with the work still on the work-bench.

:

names of masters and slaves must be separated by a / (slash).

mirror the slave axis movement, you must program the - operator before the axis name. This rule does not apply to master axes. Example:   (SDA,X/-U)  (SDA, A/B - CD) (SDA,X/AB/-14)

is slaved and mirrored to X

, C, D are slaved to A and C is mirrorhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ed to A A,B are slaved to X, and axis 14 is mirrored to X

.18 XDA – Master/Slaves axes

一个或者多个轴可以设置为另外一个轴的从属轴，而且每个从属轴可以根据一定的语法规定设置其从属类型。

主动轴和从属轴关联方法

下面的指令仅是对主动轴和从属轴进行设定，并未激活他们，要激活他们的关联性需要另外一个指令。进行了这个关联性设定后，从属轴不能被编程除非它解除了和主动轴的关联关系。  语法

(XDA, 1, master/slave1[slave2[..]],  mode, ratio, distance)

其中： master

主动轴名称。

从属轴名称，可以是：

- 字母代表的轴。

- 轴的ID号，最多8个轴。

. . . slave8

模式， 如下表格： 0 从属轴是对主动轴逐点逐点地跟随 1 从属轴是对主动轴以速度式跟随 2 3  ratio

跟随比率.是跟随的比例系数，针对的是主动轴的速度或者行程进行比例缩放。如果值等于1，那么就是相当于复制主动轴的运动，如果小于1，那么明显速度和行程减少，如果大于1，则是速度和行程放大。这个值还可以是负数。

从属轴要跟随的主动轴行程。

说明：

master axis can identify either an axis present in the process where the XDA command is activated or an axis which is not present. In the latter case, it will be created a “virtual” axis with the name

从属轴是对主动轴以位置式跟随

从http://www.wendangwang.com/doc/efe960bed681037ac6d62544属轴跟随主动轴的行程，这时候distance生效。

specified. This axis will have the dynamic characteristics taken from the slave axes (the lowest values of feed rate, accelerations and jerk). It could be either part of a virtualization (UPR, UDA,…) or of a TCP. Homing cannot be executed on master axis.

least one slave axis must be present in the process activating the XDA command; it can be a SHARED axis, i.e. an axis shared with the machine logic. It means the axis may continue to be moved by the logic machine even after the association with the master, however it cannot be moved while following the master. It cannot be part of any virtualisation or TCP. RESET deletes the Master/Slave association

下面是各种模式的阐述：

0

this mode, the slave axis follows the master proportionately to the value of the ratio (if the ratio = 1, the slave reproduces the movement of the master axis exactly), synchronisation is instantaneohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544us and the variation in the feedrate of the slave is “in steps”. Slave position and feedrate values are calculated, instant by instant, according to the following formulas:

= Vmaster * FollowRate

= PosSlavet0   (PosMaster – PosMaster t0) * FollowRate

the speed specified for the slave axis as a result of the following command exceeds the maximum admissible value for this axis, the system will reduce the feedrate requested accordingly and will give out an emergency (servo error) message, in that the slave is unable to follow the required position

[此处图片未下载成功]

1

this mode, the slave follows the feedrate of the master proportionately to the value of the ratio (if the ratio = 1, the slave copies the movement of the master axis exactly); the synchronisation depends on the dynamic characteristics of the slave axis and/or the dishttp://www.wendangwang.com/doc/efe960bed681037ac6d62544tance parameter which defines the synchronisation distance.

the distance value = 0, the slave will synchronise with the master based on its maximum acceleration and using linear ramps only.   V

t1

[此处图片未下载成功]

t

the value is not 0, the slave will synchronise with the master based on an acceleration calculated as a function of the synchronisation distance and using linear ramps only. The acceleration will be calculated again with each sampling process based on the following formula

= ((Vmaster * FollowRate)2    Vslave 2 ) / 2 * Distance

the value of the distance is gradually reduced based on the distance covered during the synchronisation stage. No check is made on the ensuing acceleration value, and therefore servo errors may arise if the acceleration exceeds the maximum value that can be withstood by the axis.

0 t 1 t

://www.wendangwang.com/doc/efe960bed681037ac6d62544rOnce the synchronisation with the master has taken place, the slave will move according to this formula:

= Vmaster * FollowRate

feedrate (Vslave) determined in this manner is “theoretical”, since it is necessary to determine whether this request is compatible with the dynamic characteristics of the axis (maximum feedrate and maximum acceleration). The moment the feedrate of the master varies, the slave will follow this variation based on its acceleration value. If the feedrate requested of the slave exceeds its maximum admissible feedrate, the system will reduce the feedrate requested accordingly. Hence, the feedrate and acceleration values with which the slave has to be moved, Vslave i and Aslave i, will be determined instant by instant. The position of the slave will therefore be calculated on the basis of these values:

[此处图片未下载成功]

PosSlave tn 1  = PosSlave tn   Vslave i   Aslhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ave i

2

this mode, the slave follows the position of the master proportionately to the value of the ratio (if the ratio = 1 the slave reproduces exactly the movement of the master); synchronisation depends on the dynamic characteristics of the slave axis and/or the distance parameter which defines the synchronisation distance.

the distance value is 0, the slave will synchronise with the master based on its maximum acceleration and using linear ramps only.

[此处图片未下载成功]

the value of distance is not 0, the slave axis will synchronise with the master axis based on an acceleration calculated as a function of the synchronisation distance and using linear ramps only. The acceleration value will be calculated again with each sampling step according to this formula

= ((Vmaster * FollowRate)2    Vslave 2 ) / 2 * Distance

the valuehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 of the distance is gradually reduced based on the distance covered during the synchronisation stage. No check is made on the ensuing acceleration value and therefore servo error messages may be generated the moment the acceleration exceeds the maximum value that the axis can withstand.

the synchronisation with the master axis has occurred, the slave will move according to the

formulas:

= PosSlavet1   (PosMaster – PosMaster t1) * FollowRate

= Vmaster * FollowRate

[此处图片未下载成功]

The position, PosSlave, and the feedrate, Vslave, determined in this manner should be rated as “theoretical” values, since it is necessary to determine whether the values requested are compatible with the dynamic characteristics of the axis (Maximum feedrate and maximum acceleration). The moment the feedrate of the master varies, the slave will follow this variation acchttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ording to its own acceleration value. If the feedrate requested for the slave exceeds the maximum value admissible for this axis, the system will reduce the feedrate accordingly. To this end, the two values with which to move the slave, Vslave i and Aslave i will be calculated instant by instant. The actual position of the slave axis will therefore be calculated on the basis of these values:

tn 1  = PosSlave tn   Vslave i   Aslave i

difference between the actual and the theoretical position of the axis is taken up by the slave during its motion (even when the master has stopped moving) by moving, to the extent feasible, at a rate higher than the theoretical value (Vslave).

3

this mode, the slave follows the position and feedrate of the master proportionately to the value of the ratio (if the ratio = 1, the slave reproduces exactly the movement of the master); synchronisationhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 depends on the dynamic characteristics of the slave.

the entire movement of the slave (i.e. both during and after the synchronisation stage), the motion of the axis is according to the following formulas (always using linear ramps):

= PosSlaveto   (PosMaster – PosMaster t0) * FollowRate

= Vmaster * FollowRate

position (PosSlave) and the feedrate (Vslave) determined in this manner should be rated as “theoretical” values, in that it is necessary to determine whether these requests are compatible with the dynamic characteristics of the axis (max admissible feedrate and max admissible acceleration). The moment the feedrate of the master varies, the slave follows the variation according to its own acceleration value. If the feedrate requested of the slave is higher than its maximum admissible feedrate, the system reduces the feedrate requested accordingly. Thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544o this end, the two values with which the axis is to be moved (Vslave i and Aslave i) will be calculated instant by instant. The actual position of the slave will therefore be calculated on the basis of these values:

tn 1  = PosSlave tn   Vslave i   Aslave i

[此处图片未下载成功]

The difference between the actual and the theoretical position of the axis is taken up by the slave during its motion (even when the master has stopped moving) by moving, to the extent feasible, at a rate higher than the theoretical value (Vslave).

the Slave(s) from the Master

instruction removes the association between the master and the slave(s). Following this instruction it will be possible to program any movement of the slave axis.  语法

(XDA)

/Changing the following ratio

instruction defines/changes the parameter that determines the ratio according http://www.wendangwang.com/doc/efe960bed681037ac6d62544to which the master is followed by the slave(s) concerned.  语法

(XDA, 2, slave1[slave2[..]], ratio) (xda, 2, slave1[slave2[..]], ratio)

其中：

. . . slave8

[此处图片未下载成功]

Are the slave axes names and each of them can be:

[此处图片未下载成功]

one ASCII character,  if the axes is programmed by name   an integer if programmed by ID

programmed by ID can refer to axes not belonging to the process, therefore they can be logical axes or axes belonging to other processes, but shared with the logics.Up to 8 slave axes per master can be programmed, 6 of which do not belong to the process.

is the master following ratio specified for the slave(s). It must be viewed as a multiplication factor for the feedrate of the master or the distance covered by it. If the value of this ratio is 1.0, the motion of the master is reproduced exactly by the slave; if it is smhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544aller than 1.0, feedrate/distance are reduced, if it is greater than 1.0 they are increased. This value can be preceded by a sign.

说明：

command can be used both when a slave is already following the master axis (it then brings about the release of the slave from the master and activates a new synchronisation stage using the new following parameter) and when the following function is not active (the command activates the following value to be used in the next movement stage).

the uppercase 语法 is used, the movement is stopped and the continuous command underway, if any, is terminated. If the lowercase 语法 is used, instead, a continuous mode command is given out; at any rate, the axes are stopped at zero speed and after that are restarted immediately. If you do not want the movement to stop, this can be accomplished by having the machine logic execute a similar command.

http://www.wendangwang.com/doc/efe960bed681037ac6d62544Activating the following function

following of the Master axis by the slave(s) is immediately activated. The following modality is defined by the “mode” parameter contained in the master/slave association command.

语法

(XDA, 3, slave1[slave2[..]]) (xda, 3, slave1[slave2[..]])

其中：

. . . slave8

the slave axes names and each of them can be:

- one ASCII character,  if the axes is programmed by name  - an integer if programmed by ID

programmed by ID can refer to axes not belonging to the process, therefore they can be logical axes or axes belonging to other processes, but shared with the logics.You can program up to 8 slave axes per master, 6 of which do not belong to the process.

说明：

the uppercase 语法 is used, the movement is stopped and the continuous command underway, if any, is terminated. If the lowercase 语法 is used, insteahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544d, a continuous mode command is given out; at any rate, the axes are stopped at zero speed and are restarted immediately. If you do not want the movement to stop, this can be accomplished by having the machine logic execute a similar command.

the following function

following of the Master axis by the slave(s) is immediately deactivated. The release modality is defined by the “mode” parameter contained in the master/slave association command.

语法

(XDA, 4, slave1[slave2[..]]) (xda, 4, slave1[slave2[..]])  其中： slave1. . . slave8

the slave axes names and each of them can be:

- one ASCII character,  if the axes is programmed by name  - an integer if programmed by ID

programmed by ID can refer to axes not belonging to the process, therefore they can be logical axes or axes belonging to other processes, but shared with the logics.You can program http://www.wendangwang.com/doc/efe960bed681037ac6d62544up to 8 slave axes per master, 6 of which do not belong to the process.

说明：

slave axis remains associated with the master, it just does not follow it any longer. Depending on the “mode” parameter defined in the master/slave association command, either of the following will occur:

The slave changes abruptly from the current feedrate to zero.

The slave comes to a halt according to its deceleration ramp.

If uppercase 语法 is used, the movement is stopped and the continuous command underway, if any, is terminated. If lowercase 语法 is used, instead, a continuous mode command is given out; at any rate, the axes are stopped at zero speed and are then restarted immediately. If you do not want the movement to stop, this can be accomplished by having the machine logic execute a similar command.

:

(XDA,1,X/ZA,3,0.8,0.0) Activates master X and slaves Z ahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nd A N20 (XDA,3,ZA) Activates following function by A and Z N30 G1X100F2000 N40 X300

(xda,4,Z) Deactivates following function by Z in continuous mode N60 X400 N70 X500

(xda,4,A) Deactivates following function by A in continuous mode N90 X660 N100 X700

(xda,3,ZA) Reactivates following function by A and Z in continuous mode N120 GX0 N130 (XDA) Removes association of slaves Z and A with master X N140 GX

2:

’s set XYZAB axes as namely 1 2 3 4 5 IDs and two logic axes point-to-to-point a b having ID as 14 and 20

(XDA,1,X/14A/20,3,0.8,0.0) Activates master X and process slave A and logic a b  N20 (XDA,3,A/14/20)   Activates following function for A, a and b  N30 G1X100F2000 N40 X300

(xda,4,/20)   Deactivates b following function  in continuous mode N60 X400 N70 X500

(xda,4,A)    Deactivates A following function in continuous mode N90 X660 N100 X70http://www.wendangwang.com/doc/efe960bed681037ac6d625440

(xda,3,/14A)   Reactivates following function by a and A in continuous mode N120 GX0

(XDA)    Releases association between slaves Z and A with master X N140 GX

3.19 AXF – Definition of axes with dynamic following function

this command it is possible to define the axes to be managed separately from the others from the dynamic standpoint. The axes defined in the following triliteral describe the programmed geometry, but move independently of the other process axes.

语法

(AXF, axle names) (AXF)

其中：

names

a nominal list of the axes to which you want the following algorithm to be  applied.

triliteral without parameters disables the algorithm on all process axes.

axes to which the dynamic following algorithm is applied are interpolated separately from the others, since with this triliteralhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 two different interpolators are created: one for normal axes and one for the axes that follow.

effect obtained is to prevent speed on the profile dropping to zero at the points where such axes start or end their movement, thereby making the entire process smoother, as shown in the example.   The axes that follow still have to be programmed.

command is activated only if there is at least one axis to which the algorithm is not applied. Each time the triliteral is programmed, any earlier following axis configuration is disabled.

axes move according to the dynamic parameters configured for them. If the speed programmed for the profile exceeds maximum admissible speed, the axes cannot work properly (Servo Error). In this case, reduce the set speed.

:

a process with 3 linear axes (XYZ) and 1 rotary axis (B), let us assume that the process is programmed as http://www.wendangwang.com/doc/efe960bed681037ac6d62544described below: (AXF,B)

XY

X100 YZAB F5000

X150 Y50 I100 J50 B90 G1 Y150

this command, the B axis is enabled to follow dynamically all the other axes of the  process

rounded corner is programmed, which becomes part of

[此处图片未下载成功]

the movement of the rotary axis:

the AXF command, the linear axes, at the start and end of the radius, come to a halt, as

[此处图片未下载成功]

axis B is added in the interpolation

the AXF command, the movement of B starts and ends on the radius but does not limit the dynamics of the linear axes: the speed on the

[此处图片未下载成功]

profile does not drop to 0

(AXF)

this command, rotary axis B is interpolated again together with the other process axes

chart shows the evolution of speed on the profile and the B axis, respectively, for the two cases described above.://www.wendangwang.com/doc/efe960bed681037ac6d62544r

[此处图片未下载成功]

radius

axis/drive parameters

in this class allow to read/write both on CNC parameters related to axis configuration and on parameters related to the axis drive.     CPA   CPD

the read/write of a CNC parameter related to an axis  Executes the read/write of a drive parameter related to the axis

.28 CPA – Read/Write of a CNC parameter related to an axis

-有关伺服轴参数的读写功能

instruction executes the read/write of an axis parameter. The majority of them matches the related configuration field in AMP, the others are additional parameters.

这个指令可以对伺服轴参数进行读写。这些参数基本上在AMP中有对应，但也有一些AMP中没有的。   语法

(CPA, mode, axis, parameter, value)   其中： mode

[此处图片未下载成功]

How to access the parameter:

= reading,  in this mode the value has to http://www.wendangwang.com/doc/efe960bed681037ac6d62544be a numeric variable otherwise a

[此处图片未下载成功]

format error is displayed

= writing, in this mode value field can be either a number or a numerical value   R = 读出，在这一模式，value必须是数字变量，否则会报格式错误；

W= 写入，在这一模式，value可以是数字变量或数字；

the axis number or the axis name, If axis is a name (alphabetical

) it has to be part of the running process otherwise system displays a format error.

理器中，否则会报格式错误；

is the numerical code identifying axis parameter. The majority of them matches in

with the related field (see the following parameters list table).

功能模式

可以是轴的ID号或参数轴名。如果是参数轴名，那参数轴名必须存在于当前运行的处

轴参数编码。基本上在AMP中有对应（见下表） value  Can be either the numerical value tgo erite or the real variable in which memorizing thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e   data read. Value             可以是数字或变量，读出时只能是变量； Charachteristics:

change of parameter by the part program is active only from the line following the programming.  The change is temporary as it doesn’t require an AMP database update. When CNC restarts, the AMP set values are restored.

does not restore the original value of a changed parameter.

can be changed by the SLAVE MONITOR and by using analog machine logic functions. CPA data function format matches the format in AMP.

parameters can’t be changed (for example the axis type);  for each of them the access mode is itemized: R (read only) and R/W (read/write).Below the parameters table (for more details see AMP manual).

说明：

参数修改后即时生效。修改是临时的，不会更新AMP， 重新启动时，会重新调用AMP参数。复位无效。 Parameters can be changed by the SLAVE MONITOR and by using analog machine logic functions 一些参数是不可修改的（例如轴类型）；

下表备注栏中‘R’表示只读，‘R/W ’表示http://www.wendangwang.com/doc/efe960bed681037ac6d62544可读写。

[此处图片未下载成功]

以下是AMP 之外的参数:

[此处图片未下载成功]

[此处图片未下载成功]

more details on how to use all the parameters,please refer to the AX_WPAR machine logic function presented in “PLUS Library” and WinPLUS Library” manuals.

更详细的说明参照“PLUS Library”和“Winplus Library”手册的“AX_WPAR”指令功能。

1:

’s say you want to change the rapid acceleration parameter in AMP (RAPID_ACCELERATION) writing 2500 mm/sec2 for the Y axis (as 2) in the running process. The following commands are equivalent: (CPA, W, E0, E1, E2)   con E0 = 2,  E1 = 12 e E2 = 2500 (CPA, W, 2, 12 , E2) (CPA, W, Y, 12 , 2500) 举例：

假如要修改AMP当前处理器Y轴快速进给加速度参数（RAPID_ACCELERATION）为2500mm/s/s，可用以下任一条程序

(CPA, W, E0, E1, E2)   con E0 = 2,  E1 = 12 e E2 = 2500 (CPA, W, 2, 12 , E2) (CPA, W, Y, 12 , 2500)

[此处图片未下载成功]

.29 CPD – Drive Parameters Read/Write

-有关伺服驱动器参数的读http://www.wendangwang.com/doc/efe960bed681037ac6d62544写功能

instruction executes the read/write of a drive parameter related to a digital axis. CPD指令执行对数字轴驱动器参数的读写

其中： mode

(CPD, mode, axis, parameter, value, format

[此处图片未下载成功]

)

to access the drive parameter:

= reading,  in this mode the value has to be a numeric variable otherwise a format error appears

= writing, in this mode value field can be either a number or a numerical value

R = 读出，在这一模式，value必须是数字变量，否则会报格式错误；   W= 写入，在这一模式，value可以是数字变量或数字；

功能模式

the axis number or the axis name, If the axis is a name (alphabetical character) it has to be part of the running process otherwise system  reports a format error.

可以是轴的ID号或参数轴名。如果是参数轴名，那参数轴名必须存在于当前运行的处

理器中，否则会报格式错误；

This is the numeric code identifying the axis phttp://www.wendangwang.com/doc/efe960bed681037ac6d62544arameter. The majority of them matches in

with the related field (see the following parameter list table).

轴参数编码。基本上在AMP中有对应（见下表）

[此处图片未下载成功]

be the numerical value to be written or the real variable in which memorizing the data format. For drives having OS-Wire or D.S.I, interfaces, the field is not important, Let’s set value 0.

可以是数字或变量。对于OS-Wire 或 D.S.I通讯的驱动器，这一栏是不重要的，设0. For drives with Mechatrolink  interface, let’s set as follow:

bit  0 (parameter dimension) = 0 parameter on 2 bytes (word)               = 1 parameter on 4 bytes (long)   bit 1 (access)               = 0 access in RAM               = 1 access in EEPROM

对于Mechatolink总线通讯的驱动器，设定如下：

bit  0 (参数字长)                    = 0  2 bytes (word)

1:

’s say you want to read the speed loop proportional http://www.wendangwang.com/doc/efe960bed681037ac6d62544gain  parameter  (cod. param. = 5004) set for Z axis (id = 3) on a OS-WIRE drive. Commands below are equivalent:  (CPD, R, E0, E1, E2, E3)   con E0 = 3,  E1 = 5004 e E3 = 0 (CPD, R, 3, 5004, E2, 0)

, using the command:

(CPD, R, 3, 5004, 2.5, 0) -&gt; system identifies format error as the destination variable is not specified.    举例：

假如要读取OS-WIRE驱动器z轴（id=3）速度环比例增益（cod.param.=5004）.可以用以下任一程序段  (CPD, R, E0, E1, E2, E3)   con E0 = 3,  E1 = 5004 e E3 = 0 (CPD, R, 3, 5004, E2, 0)

若用以下程序段，则会报格式错误：  (CPD, R, 3, 5004, 2.5, 0)

= 1   4 bytes (long)          = 0  RAM          = 1  EEPROM

1 (存储模式)

.30 工作原点和坐标控制码

在这个分类中的字母执行下列操作： G 代码 G09 G16 G17 G18 G19 G27 G28 G29 G70 G71 G79 G90 G91 G92 G93 G94 G95 注意：

如果他们以下列顺序设置: X, Y 和 Z，那么G17，G18，G19所定义的平面有效。

作用

程序段运动终点做停留   程序段运动终点做减速 定义插补平面

在XY平面上的圆弧插补和直径补偿 在ZX平面上圆弧插补和直径补偿 在YZ平面http://www.wendangwang.com/doc/efe960bed681037ac6d62544上圆弧插补和直径补偿 在拐角处上连续移动且自动减速 在拐角处上连续移动，不减速 点对点移动 以英寸为单位编程 以毫米为单位编程

以绝对坐标系编程（归零点为0） 绝对型编程 增量型编程 工作原点预设

时间倒数(V/D)进给率编程模式 进给率编程，以ipm 或mmpm为单位 进给率编程，以ipr或mmpr为单位

3.31 G17 G18 G19 -  选择插补平面

编码用于定义下面的插补平面，描述如下：

[此处图片未下载成功]

G18   G19

轴1 (X), 2 (Y), 和 3 (Z)是在AMP环境中定义的前3个轴。  语法 G17 G18 G19

采用由轴1和2(XY)形成的插补平面。

[此处图片未下载成功]

采用由轴3和1(ZX) 形成的活动插补平面。

[此处图片未下载成功]

采用由轴2和3 (YZ) 形成的活动插补平面。

.32 G16 -  定义插补平面

像G17,G18,和G19一样，G16定义插补平面，但它要指出横坐标和纵坐标，就是具体设置需要指定两个轴的名称来确定这个指定平面。  语法

axis1 axis2   其中：

插补平面横坐标的名字（通常为X）。其必须是系统中设置的轴之一。 axis2 插补平面纵坐标的名字（通常为Y）。其必须是系统中设置的轴之一。  说明：

如果以下G码被起用，则G16, G17, G18, G19不能被使用： 直径补偿(G41-G42) 标准固定循环(G81-G89)  示例： G16 X A

指定由轴X和A形成的插补平面。

3.33 G27 G28 G29 -  定义运动模式

在这个分类中的G字母定义轴是如何在轮廓上移动的及如何在轮廓末端定位的。

[此处图片未下载成功]

在拐角处上连续运动且自http://www.wendangwang.com/doc/efe960bed681037ac6d62544动减速。减速过程由控制器自动计算和根据轮廓形状优化方式来决定。计算基于DLA, MDA和VEF值。

[此处图片未下载成功]

G28  G29 0。 语法

[G-codes] [operands] G28 [G-codes] [operands] G29 [G-codes] [operands]   其中： G-codes   operands   说明：

下图显示了G27, G28和G29是如何作用的，当编程的进给率一定时。

[此处图片未下载成功]

[此处图片未下载成功]

在拐角处上连续的运动但不减速。轮廓上的速度等于编程的进给率。

[此处图片未下载成功]

点对点的运动，其独立于编程了的路径字母(G01-G02-G03)。在每个拐点处，轮廓上的速度是

同G27, G28和G29兼容的其他G编码（见第一章“兼容的G编码”表）。 可以用在G字母程序段中的任一运算值或编码。

[此处图片未下载成功]

G29

下图显示了G27, G28和G29是如何作用的，当编程的进给率变化时。

[此处图片未下载成功]

[此处图片未下载成功]

G28

[此处图片未下载成功]

在每个程序段中，移动分为三步： 1) 加速 2) 3)

和G28的区别是否有减速动作。在连续模式(G27, G28 and G29)中，以加工速率定位(G1, G2, G3)是有效的，而快速定位(G0)总是点对点的，即定位完全后降速至零，G0只关心最终的位置精确度。

用G27-G28（连续模式），控制器执行轮廓加工，就把运动过程视为只是一个单一程序段一样看待。由于这个原因，辅助字母M, S 和T不允许用在G27-G28执行的轮廓过程中被编程。 连续模式可以由G00暂时关闭http://www.wendangwang.com/doc/efe960bed681037ac6d62544，然后允许M, S和T字母在G00后的程序段中编程。  注意：

在AMP中设置的G编码（通常是G27）在通电或在重设后会自动起用。

以编程的进给率统一移动 减速的动作

示例：

这是在连续和点对点模式下的轮廓加工示例。

[此处图片未下载成功]

程序1（连续模式）：  (UGS,X,-400,100,Y,-400,100)   N9 (DIS,&quot;MILL DIA. 16&quot;)   N10 T4.4 M6 S800 1 N11 G X-235 Y-230 M13   N12 Z-10 2  3 4 5              N13 G27 G1 X75 F500  ; 连续模式开始（G27） N14 Y .

G3 X-70.477 Y25.651 I J N16 G1 X-187 Y-295 N17 G Z5 M5

; 暂时转到点对点模式

(DIS,&quot;MILL DIA. 28&quot;) ; 用于主轴停止，刀具转换和S字母等执行 N19 T5.5 M6 S1200 N20 X.. Y.. M13 N21 Z-..

G1 X.. Y.. ;  连续模式继续执行

如果G29在程序段N17中被编程，连续模式会停止，后面的在G1-G2-G3的移动会以点对点模式执行。

程序2（点对点模式）：    1    2 3  4    5

(UGS,X,-400,100,Y,-400,100) N9 (DIS, &quot;MILL DIA. 16&quot;) N10 T4.4 M6 S800

G29 G X-235 Y-230 M13 N12 Z-10              N13 G1 X75 F500 M5

;  主轴停止

Y S1200 M13 ; 主轴顺时针旋转并开启冷却。 N15 G3 X-70.477 Y25.651 Ihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 J N16 DWT=2

G1 G4 X-187 Y-295 ; 在末端稍作停留 N18 G Z5 M5

(DIS,&quot;MILL DIA. 28&quot;) N20 T5.5 M6 S1200 N21 G X.. Y.. M13 N22 Z-..

G1 X.. Y..

在程序段N11中，用G29起用了点对点模式，M和S字母也在加工过程中被编程了（程序段13和N14）。另外，DWELL（程序段N17），也能在连续模式下被编程。

; 点对点操作开始

G27模式中的自动减速

当G27模式激活时，控制器会用一个两步算法自动计算拐角处上的向量速度。

在第一步中，向量速度用基于轮廓变化的算法计算。轮廓的变化同后续两个动作形成的角度相关。

控制器将实际角度与MDA值比较；如果实际角度大于它所设的值，向量速度会定为0，如G29模式中一样；否则，控制器将会基于这个角度，MAD和VEF值来计算。

算法的第二步，称为“前瞰”，是可选的。根据DLA的值来启用或者禁用。

“前瞰”是第一步的优化。实际上，鉴于G27发挥其作用时的距离总长度和各个轴的减速设置，为了在轮廓末端提供一个正确的停止，这个向量速度便被重新处理过了。   前瞰(G1 G27)不处理超过100%进给率的情况，更高的进给率可能产生SERVO ERRORS。

.34 DLA – 减速前瞰

启用/禁用G27运动模式中的前瞰功能，控制器读取组成该轮廓的程序段以及后续的一些程序段，目的是计算出一定的速度来迎合不同的程序段，当然它也会计算拐角处的减速。如果轮廓中包含了急变的轨迹然而又没有足够的程序段所描述的点来缓和适当的减速，对于控制器来说严格地预判到这些情况然后做出调整是有必要的，从当前所执行的程序段开始预判后续的程序段数量可以指定，范围是2到64。   语法 DLA=value   其中:

can be: 0   注意:

如果http://www.wendangwang.com/doc/efe960bed681037ac6d62544DLA为1则系统程序段执行时间会增加，这是由于控制器得去执行更多的一些额外计算，但会增强了精确度。

如果很清楚所加工的轮廓轨迹，以至在连续运动模式下能够保证良好的减速和停止，则建议把DLA设为0。. DLA设为0之后，控制器只会专注于拐角处的偏离程度。  说明：

默认值在AMP中被设定。

禁用前瞰 启用前瞰

.35 DYM – Dynamic Mode

是定义在G27模式下采取的相邻两个运动点之间的速度算法，配合VEF和MDA使用。  语法： DYM=value  其中：

代表的是一个数字，可以是：

采用标准 10 系列计算公式 1 采用标准 8600 系列计算公式 2采用第二套 10 系列计算公式  3采用第三套 10 系列计算公式

以上数值加100则同时启用了JERK控制和最小斜坡运行时间。

最小斜坡运行时间是指每个运动程序段最小要执行的时间，特别当一系列很密集的程序运动点相连且拐角剧烈时，可以设定该值使每个程序段至少执行这个最少时间从而得到缓冲。

standard Series 10 algorithm is based on precise mathematical formulas which assume a linear response from the machine and that the dynamic parameters configured are always applicable under any condition.

algorithm already present in the 8600 series uses approximate formulas, therefore applying greater restrictions on movement.

alternative algorithms keep into consideratiohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544n the dynamic components (acceleration) that the axes can bear when passing from one block to the other. In this way it recalculates the final speed at of the first block in order to pass to the next one without excessive stress on the machine.

is recommended that you verify the behaviour of both algorithms on the machine and  Characteristics

default value of this variable can be set in AMP.

dynamic analysis, calculating the suitable speed rate and infeed/exit from circular trajectories (G02/G03), is activated when adding 100 to the DYM variable, This procedure avoids high speeds along the circumference as well as oscillations when entering or escaping a circular motion.

lines speed rate computation is based  both on the jerk and on the minimum ramp time related to the axes within the movement. Limitation is based on the circumference radius.

passing from lines to circumferenchttp://www.wendangwang.com/doc/efe960bed681037ac6d62544es (and vice versa) and from a circumference to another, additional speed diminutions are activated in relation to the jerk of the axes involved.

considers the curve variation (radii variation in case of circle/circle and radius variation in a line/circle case) in order to set suitable speed rate to/from circle moves not leading to oscillations on the part.

.36 MDA – 最大减速角度

定义的是采用G27运动模式的最大允许拐角值（0到180度），大于这个角度值则不采用G27拐角减速控制，而是变为0。  语法 MDA=value   其中: value

其可以是以下数值：

[此处图片未下载成功]

角度值0&#176; 到180&#176; 如果

[此处图片未下载成功]

DYM = 0 and DYM = 3  数值 0 and 2 如果 DYM = 1

特征:

如果想改变MDA的值，可以在程序上给MDA赋值或者通过MDI输入框输入，或者在AMP上编入。   当系统遇到偏离角度大于MDA设定值，则速度会在拐点处降到零，如果拐角小于或者等于

定义的角度，那么系统自动计算进行减速。

遇到复位命令会恢复AMP中定义的数值。

两种情况下，都是代表两个连续的运动线段之间的拐角。 如果 DYM = 1, 它的值得计算公式如下: 夹角的正弦值 ，当   90&#176;

sine (夹角- 90&#176;) ，  http://www.wendangwang.com/doc/efe960bed681037ac6d62544 当 &gt; 90&#176; 且   180&#176;.

[此处图片未下载成功]

DYM = 2，MDA不起作用

示例: DYM=0 MDA=90&#176; MDA=180&#176;

=1 MDA=1 MDA=2

3.37 VEF – Velocity Factor

是调整G27模式下拐角的减速度，结合MDA来确定这个拐角速度。  语法 VEF=value

其中： value

可以是以下数值：

[此处图片未下载成功]

说明：

不同的DYM数值下，VEF有着不同的含义：

= 0

以下的图表示了固定的MDA设定值情况下不同的VEF值产生的减速效果。

[此处图片未下载成功]

.1 到 8   0 到 99999  -1 到 99999 0 到 99999

如果 DYM = 0 默认值为

[此处图片未下载成功]

0.8. 如果 DYM = 1 默认值为

[此处图片未下载成功]

0.8. 如果 DYM = 2 默认值为

[此处图片未下载成功]

0.8 如果 DYM = 3 默认值为0.8

其中： V

拐角速度 拐角角度 编程速度

= 1

定义拐角轮廓的最大偏离值，即加工误差，如果数值是0，那么拐角处会减速直至0后再继续前进。

DYM = 2

定义的是拐角最大速度，如果VEF=0.8，那么拐角速度最大是1 0.8=1.8倍working acceleration，如果是VEF=0.3，则拐角速度最大是1-0.3=0.7倍working acceleration。由于同时插补的几个轴的worhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544king acceleration可能不同，那么系统会采取最小的那个轴的速度。

= 3

这时VEF表示时间，单位为毫秒，通过它和所设定的加速度可以获得拐角的速度值，公式如下：

= Acceleration * VEF

：拐角速度 Acceleration：加速度

由于 VEF单位是毫秒而Vcorner 是毫米/分钟，加速度是毫米/秒&#178;，那么完整的公式如下：       Vcorner * 1000 VEF=

* 60

system will calculate the speed on the edges according to all the axes that are part of the movement; each axis will have a different speed and the system will choose the minimum among these.系统会分别计算各个轴在这个拐角的分速度，   A system RESET restores the VEF value configured in AMP

3.38 CRV – Curve – Feed rate optimization parameter

optimizes the programmed feed rate value along curves designed by a packed points sequence or by a “noise” sequence on smooth paths.  语法：

= Value   value  说明：

如果一个加工路径是由一序列的点或者弧组成的，而且路径形成的角度非常小，在这种情况下，由于速度比较快，经过每一个小段的时间很短（有时候还会直接跳过），于是在这个路径会产生加工误差。

考虑的接下来的加工路径的拐弯幅度http://www.wendangwang.com/doc/efe960bed681037ac6d62544从而控制加工速度，而CRV是一个时间值，当前速度倘若不变的话，它乘以这个时间值便会得出一个距离，所以系统判断以当前这个点的速度经过这个时间去到哪一个点，然后该点和起点切线的角度变化是多大，再根据MDA或者VEF修正起点的速度。接下来的每个拐点继续使用这个法则。

还可以避免在一个平滑的路径下遇到一个极短的起伏点进行紧急减速，从而保持该平滑路径的光滑度。 Higher values could lead to “deficit elements” issue as, before starting a move, they could require the analysis of several following moves (as per the look ahead).通常CRV介于4.0和6.0之间是一个比较理想的数值，

[此处图片未下载成功]

左侧是由一系列rectilinears组成的曲线，第一个线段产生的角度只有11.25&#176;，但是总的拐角显然是90&#176;，如果CRV=0（也就是不使用CRV功能），那么在第一个线

是一个正数表示时间，单位为毫秒，用来获得待考虑的曲线范围，如果设置成0，则相当于取消该功能。

该功能只在G27，G28下有效。

段的速度会很高，因为系统不知道后面的情况。

左边是第二种情况，本来这个路径是一个直线，但当中有一个小瑕疵，产生了一个干扰，如果不使用CRV，那么系统会减速以通过这个瑕疵点，如果启用了CRV，那

么系统就不减速，按原来速度直线越过该瑕疵点。

.39 MOA – Motion Auxiliary

语法：

= value

其中：

可以是 0 或 1, 它启用/禁用“null motion threshold”功能。  说明：

每个轴在 AMP 里面可以设置null motion threshold（不动作范围）。

://www.wendangwang.com/doc/efe960bed681037ac6d62544par如果加工程序里面有一段移动距离小于这个范围，那么组成该运动的各轴不会进行任何运动，即忽略该点的运动，特别是一个移动距离在1μm的情况下，但具体需要参考是否小于null motion threshold的值，默认值是1μm。

则是用来开启或者禁止null motions threshold。

.40 Jerk 介绍

是加速度对时间的微分，轴加速过程中，加速度是从零开始达到额定加速度，待轴速度将要达到目标速度时，加速度又会慢慢递减直到0，同时速度也达到目标速度。所以加速度数值不是一开始就是额定加速度，而是有个逐渐变化的过程，同理减速的时候也一样。这样做的目的是为了使运动半径平滑，加工效果更理想，Jerk加大，则运动起点和终点速度变化就更剧烈，可能产生机器的颤动，所以Jerk的设定依据具体的机器特性而定。

(t)

[此处图片未下载成功]

3.41 MOV – 应用于Jerk设定

语法： MOV = value 其中： value

“rapid”braking Movements change optimization during profiling with G27/G28 非线性加速模式（S型加速）

可以是一个数值，指定方案编号。

该数值是以下二进制值进行十进制转换而得。

启用Jerk系数

management of rotating axes with UPR 2 or 6

of Trapezoidal Ramps Recalculation of machining speed

加工程序中的进给率只应用在直线轴 手动模式下轴移动时启用VFF

的默认值是0，在AMP可以修改该值。 示例：

如果你想采用非线性加速模式（S型加速），而且启用Jerk系数，那么MOV的值则是2 2&#178;=6

://www.wendangwang.com/doc/efe960bed681037ac6d62544r[此处图片未下载成功]

位元1，3 和5：  位元1：

启动非线性加速模式（S型加速），加速度并非恒定，而是从0平滑地增加到目标最大加速度（注意所述的是加速度并非速度），目标最大加速度是A/JRK，JRK后续章节中会提及到。所以当JRK=1，则加速度会达到AMP轴参数中的加速度值，如果JRK=2，则只达到轴参数中加速度值的一半，如果JRK=0.5，则会达到2倍轴参数的加速度。The ensuing jerk values on the movement will NOT be controlled and will range from 0 to an undetermined value.

Speed

在上图的例子中，达到速度20000毫米/分，加速度是1500毫米/分钟&#178;。另外可以看到，加速度最大值出现在加速过程中的中点位置，此后虽然速度仍然增加，但加速度实际上是开始下降。在减速过程中则刚好相反，最大减速度出现在减速过程中的中间。

因为是S型的加减速过程，不方便准确计算加速或者减速过程所需时间，如果要计算此时间，可以参考以下公式：

= T linear ramp * JRK * 1.485.

:  总的加速或者减速时间

linear ramp： 目标速度/AMP轴参数中设定的加速度

Minimum ramp time（最小斜坡加速时间）会影响以上算式，假如按以上算式算出来 的结果比Minimum ramp time还小的话，那么它会被Minimum ramp time的数值替代。

: The minimum ramp time is time it takes to reach the maximum acceleration value (Jerk application time) so that, as can be seen from thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544he chart below, the total ramp time corresponds to twice the minimum time.

application time

位元3  ：

the non linear ramps (ramps with jerk limitation). Acceleration ramps are calculated on the basis of the jerk parameters configured in AMP. The jerk value used within a movement is calculated by the system so as to ensure that the movement complies with the jerk characteristics specified for each axis. The jerk value configured for each axis must be construed as the maximum value that can be reached during the acceleration stage. The system modulates the jerk value continuously between 0 and its maximum value, and it will modulate in the same manner the acceleration value, which will not necessarily reach the maximum value configured.

Speed

the example above, a movement at a speed of 2http://www.wendangwang.com/doc/efe960bed681037ac6d625440000 mm/min with an acceleration of 1500 mm/sec2 and with jerk of 15000 mm/sec3 has been programmed. The maximum acceleration value is reached only at a time halfway between the acceleration stage or the deceleration stage and it is below the maximum value that is requested. Only with a higher jerk it will be possible to reach the maximum acceleration.

time is affected by the jerk parameter and by the “minimum ramp time” parameter configured in AMP for each axis. If the time calculated for the ramp does not meet the minimum ramp time limit, the ramp will be recalculated to comply with this requirement.

: The minimum ramp time is time it takes to reach the maximum acceleration value (Jerk application time) so that, as can be seen from the chart below, the total ramp time corresponds to twice the minimum time.

Speed

application

5  (vahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544lue 32) :

the non linear ramps (trapezoidal ramps). Acceleration ramps are calculated on the basis of the jerk parameters configured in AMP. The jerk value used within a movement is calculated by the system so as to ensure that the movement complies with the jerk characteristics specified for each axis. The jerk value configured for each axis must be construed as the value that can be used during the acceleration stage. The system keeps the jerk value continuously during the acceleration stage.

the example above, a movement at a speed of 20000 mm/min with an acceleration of 1500 mm/sec2 and with jerk of 15000 mm/sec3 has been programmed. The maximum acceleration value is reached and maintained for a certain time in the central part of the acceleration or deceleration stage; it may or may not reach the maximum value requested as a fuhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nction of speed leap to be made.

time is affected by the jerk parameter and also by the “minimum ramp time” parameter configured in AMP for each axis. If the time calculated for the ramp does not meet the minimum ramp time limit, the ramp will be recalculated to comply with this requirement.

The minimum ramp time is time it takes to reach the maximum acceleration value (Jerk application time).

application

说明：

linear ramps work both on point to point movements (G29) and continuous movements (G27 and G28). The activation or deactivation of non linear ramps in a continuous movement is not perceived, it is only perceived in point by point movement mode. Similarly, it is not permitted to change from G27 to G28 (and vice versa) if non linear ramps are active; in such circumstances it is necessary to close thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544he continuous movement (G29) and open another according to the new modality.

is recommended to use value 8 for machines with high dynamic levels (high jerks), while value 32 should be used in machines where dynamic levels have to be reduced (low jerks). Configured jerk being the same, value 32 performs better (in terms of execution times) than value 8, but engenders more “abrupt” movements.

of bit  0:

0 (value 1):

change optimization during profiling with G27 and G28. This option must be used particularly for curves defined “by point”. It allows a better management of the profile curve variation (especially if defined with very short movements) avoiding axes movements out of the profile. This option is activated by default in the case of non linear ramps.

of bit 2:

2 (value 4):

NON-linear ramps, this option enables the rapid http://www.wendangwang.com/doc/efe960bed681037ac6d62544braking mode in case of RESET, HOLD, FeedHold, CycleStop, Override at 0. In all these cases, the movement involves S ramps (MOV=2), considering only the accelleration value along the profile, ignoring Jerk and minimum ramp times.

Prima Electro S.p.A.Type of manualMeaning of bit 4: Bit 4 (value 16): enables the type of rotary axis speed management mode to be adopted with UPR 2 or 6 active; if this bit = 0, standard management is maintained; if this bit = 1, the rotary axes will use different speed diagrams. In the former case, the positioning of the rotary axes conforms to the transformation requested by the UPR, but the particular computation algorithms employed may cause appreciable showdowns around singular points. In the latter case, slowdowns are eliminated, but the positioning of rotating axes may fail to conform to the transformation requested by the UPR: in such cases, the axes will lag behind. Since thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544is occurs around singular points (mostly with vertical tool axis), the rotary axis positioning delay has virtually no effects on processing results. Meaning of bit 6: Bit 6 (value 64): defines that the feed rate programmed in a movement block refers to linear axes. The programming of a rotary axis, in addition to the linear axes, entails an automatic recalculation of the speed so that it remains the same along the linear axes. The recalculation of the speed is only applied if both the linear axes and the rotary axes are present in a movement. It is not applied in the case of circular movements (G2/G3) in which a rotary axis is part of the interpolation plane.This feature must NOT be activated if speed programming is executed in G93 or with t. In this case, the resulting machining time would not be correct.Meaning of bit 7: Bit 7 (value 128): enables the VFF algorithm also for manual movements that are normally executed using thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e “tracking error” algorithm only.45004457K81

Prima Electro S.p.A.Type of manual3.42JRK – Jerk 系数The JRK code defines the acceleration management mode during the execution of movements with S ramps (MOV=2). 语法： JRK = value其中： valuea numeric value greater than 0.5, which is used to define the acceleration management mode in a non-linear ramp说明： 默认值为 1. The JRK value can be configured in AMP. The RESET command restores the default value. By setting JRK = 1, the acceleration ramp retains the values configured for axis accelerations. Acceleration increases with a value lower than 1, and decreases with a value higher than 1.  AccelAccelIt is necessary an acceleration of 1500 mm/sec&#178; in both movements. In the first movement has been used JRK=1 so that the nominal acceleration value is reached, in the second case has been used JRK=2 so that half the nominal acceleration value is reached. In the nehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544xt example has been used JRK=0.5 so that twice the nominal acceleration value is reached.Accel45004457K82

Prima Electro S.p.A.Type of manual3.43JRS – Jerk Smooth ConstantThe JRS code defines the threshold value for limiting the speed with Jerk Limitation activated. Sintyax: JRS = value其中： value is a a numeric value greater than 0, which used for defining a speed threshold below which the speed is to be limited if the programmed speed cannot be reached. 说明： A characteristic of the lookhead algorithm for Jerk Limitation is that it avoids continuous acceleration and deceleration that would cause oscillation in the movement of the axes. This could happen if the if the programmed axes do not allow the speed set (Vi) to be reached. To this aim, the speed diagram is &quot;cut&quot; as illustrated in the figure below:ViVVi Eliminated parts Vit To prevent the &quot;cut&quot; part from being too large and http://www.wendangwang.com/doc/efe960bed681037ac6d62544considerably increasing the machining times, a threshold below which the speed is to be limited is defined.This threshold is calculated as a function of the JRS parameter on the basis of the following rule: Vmax The maximum speed value calculated by the algorithm on the movements taken into consideration Vmin The minimum speed value calculated on the movements taken into consideration. The system checks whether | Vmax - Vmin |&lt; Vmin   JRS If it is, the Vmax is set equal to Vmin, otherwise it is recalculated so that there is a section with a constant speed in the upper part of the ramp. 默认值为 1. The RESET command restores the default value.45004457K83

Prima Electro S.p.A.Type of manual3.44MBA – MultiBlock retrace Auxiliary functionsThe MBA (Boolean) variable makes it possible to enable/disable the auxiliary functions (M functions) during Retrace operations: 语法： MBA = value说明： The emission of auxiliary fhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544unctions is performed only during forward retrace (see user manual) value = 0 Emission disabled value = 1 Emission enabled After a reset, the variable is reset with the value configured in AMP.45004457K84

Prima Electro S.p.A.Type of manual3.45REM – Automatic return to profiled at end of moveThe REM (Boolean) variable determines the Jog return mode. If the variable is set on 0 the return point is the point at which the hold stage begins (standard execution). If the variable is set on 1 the return point is the final point of the movement in which the hold stage begins. The return movement is performed automatically, without manual movements (JOG). 语法： REM = valuevalue = 0 Return to input point in hold value = 1 Return to input point at end of movement Reset does not modify the value of the variable.3.46IPB (DTL) – 确认定位完成范围设置语法： (IPB, axis1,[axis2,. . .,axis9])其中： axis1 . . axis9 说明： 指定在 G00 或者 G29 模http://www.wendangwang.com/doc/efe960bed681037ac6d62544式下在每个运动程序段的终点实际位置和编程位置的偏离距离，各轴执行下一个运动 前需要先定位在这个偏移距离以内，也就是确认到位之后才继续往下执行。如果 IPB=0，则采用 AMP 所设定 的 In position Band 的值。 在以下情况下使用 IPB 命令会报错： 直径补偿应用中(G41-G42) 连续运动模式(G27-G28) In internal computations the value entered is rounded out to &lt; 1 digit. The error generated is NC 133. Before programming an IPB command you must disable these codes from program. 程序中的 IPB 指令会覆盖 AMP 里面的数值，复位并不会恢复 AMP 的默认值。 轴编号，最多可以设置 9 个轴。示例： (IPB, X 0.1, Y 0.05) 指定 X 的定位范围是 0.1 毫米而 Y 轴的定位范围是 0.05 毫米。45004457K85

Prima Electro S.p.A.Type of manual3.47MOM – Manual Operating ModalityMOM sets the manual moves execution (jog). The operating features in manual moves define different axes control modes. 语法： MOM = Values说明： Value = 0 (as up to Fixup 8 Release 7.6) MOM has two different modes depending on how many axes are manually moved; in both cases, axes can move only within their operational limits (if active). During a manual movement on http://www.wendangwang.com/doc/efe960bed681037ac6d62544one real axis (a non virtual axis or a tool direction), the move is programmed within the operational limits preset in the axis motion parameters. Once the limit is reached, the axis brakes using its own manual acceleration. This move is active only after the axis selection managed by the user interface (WinNBI, Human Interface, …). For manual movements concerning multiple real axes or for movements along a virtual axis and/or tool direction axis, the resulting movement has no limit for axes movement, a specific look-ahead algorithm checks if the axis exceeds the operating limits. When the algorithm estimates that the limit will be exceeded the system generates an emergency and each axis stops using its rapid deceleration. This implies that if a virtual axis (for instance W axis in tool direction) was moving, the corresponding stopping cannot happen along the (virtual) axis direction, since each axis stops using its deceleration vahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544lue, so the original trajectory CAN’T BE respected. Only machine Logics can activate this axes selection. All stopping generated when reaching operating limits uses “S” ramps and ignores the value of the JRK variable; as a consequence the accelerations can exceed, during the central phase of stopping, the value of rapid acceleration. The mean acceleration for the stopping is, however, equal to rapid acceleration.Value = 1 In the case of a single real axis nothing changes with respect to mode 0. In all the other cases, movement involving more than one real axis or along a virtual axis and/or tool direction, the system uses new algorithms to forecast and to brake when reaching operating limits. When there is a move along the tool direction axis or along UPR virtual axes, a forecast of when the operating limits will be reached is made considering the direction of movement along the virtual axes in use. As soon as the forecast positihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544on is reached, controlled deceleration is made along the virtual axes using the virtual axes manual acceleration. In that case, the original trajectory defined by the virtual axes is maintained. Axes are stopped using a controlled stop (using manual acceleration) on the axis that reaches its limit and not by generating an emergency. All other axes can continue in their movement. For example, moving simultaneously the virtualization UPR of a P axis and the A axis, reaching the P operational limit (i.e. the limits of the XYZ real axes) will cause only the P axis to stop (XYZ) and not A axes.45004457K86

Prima Electro S.p.A.Type of manualIf TCP is active, the move operational limit (axes or tool direction) is checked in realtion to the axes position. Control can be activated for the tool head as well and can be set axis by axis. In that case, the “Operating Limits Mode” within the “Dynamic” table of the TCP configuhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ration (L367) is used. Bits 1, 3 and 3 (starting form bit 0) activate the operational limit control referring to the tool headnamely for the first, the sendo and the third TCP axis. For example, by assigning value 7 to the L367 variable, operationa limits realtime control is activated for both the tool head and for the X and Y axes positions, keeping active for Z only the control reffered to the physic position.Forecast operational limits reaching algorithm on each physical axis is kept active in order to control limits when the axis move is performed by different components (for example, in the TCP case, the compensation made by the movement of a rotary axis is added to the compensation of the linear axis). Algorithm behavior is modified in order to: to stop only the moves that cause the movment of the axis exceeding the operational limits; for example, in the TCP case, if the limit is set on liner axis X, all the rotary axes arhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e stopped as leading to a move of the X axis, but not to a move of Y and Z. Similarly in the UPR case, only the virtual axis (P) moving the X axis is stopped when UPR,0,XYZ,PQD,0,0,0, while all the vistual axes are stopped when UPR,0,XYZ,PQD,10.0,10.0,10.0. In the TCP case, 5, all the move on W will be stopped once the limit of one of the linear TCP axes is reached. to stop with no emergency; axes selected for the manul move will stop using their rapid acceleration.If TCP,5, is active, this mode allows to move at the same time the tool direction axis (W) and all the other axes, no matter if related or not to the TCP. All stopping generated when reaching operating limits use “S” ramps and ignore the value of JRK variable; as a consequence the accelerations can exceed, during the central phase of stopping, the value of rapid acceleration. The mean acceleration for the stopping is, however, equal to rapid acceleration. Value = 2 It http://www.wendangwang.com/doc/efe960bed681037ac6d62544behaves as 1. In this mode the braking phase is extended to all the axes , not only to the ones reaching operational limits and their associates.45004457K87

Prima Electro S.p.A.Type of manualValue = Value   16 It has to be considered as 16 value added to 0, 1, 2 value. This value is used according to a UPR, 8 presence during the manual move. During a manual move using UPR, 8, the rotary plane has to be recalculated according to the orizontal rotary axis move, in order to move virtual axes matching the head position After the manual move, the starting UPR tern is usually restored. When the move stops, ddding 16 to MOM, the tern is kept oriented according to the rotary axes position. Value = Value   32 It has to be considered as 32 value added to 0, 1, 2 value. This value is used according to a UPR, 8 presence during the manual move. During a manual move using UPR, 8, PQ axes (the first two virtual axes active onhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 UPR) are moved using dynamic charatcteristics lower than the one of the two real axes (XY); for example, the lower velocity between X and Y and the lower acceleration between X and Y. Adding 32 to MOM, axes will move with lower dynamic characteristics but the velocity; P axis wil move at X velocity and Q axes with th Y one.45004457K88

Prima Electro S.p.A.Type of manual3.48G70 G71 - 测量单位G70 和 G71 编码定义控制器使用的测量单位。 G70 G71 语法 G70 [G-codes] [operands ] G71 [G-codes] [operands ] 指定英寸编程 指定毫米编程其中： G-codes operands 说明： 如果 G70 和 G71 都没有被编程，系统会假设为在系统设置中存储的默认测量单位（通常为 G71）。 当系统从 G71 转换至 G70 或从 G70 转换至 G71，系统同时会转换所有的位置和进给率信息到相应的单位。 然而，当系统在 G71 和 G70 之间转换时，补偿值和工作原点表不会自动转换到相应的单 位。 G70 和 G71 之间的转换不会影响从探测循环 G72, G73 和 G74 读取的值。 同 G70 和 G71 兼容的其他 G 编码（见第一章“兼容的 G 编码”表）。 可以用在 G 字母程序段中任一运算值或编码。45004457K89

Prima Electro S.p.A.Type of manual3.49G90 G91 G79 – 绝对，增量和归零点编程这些 G 编码定义编程模式是否是绝对的，增量的或参考机器归零点的。 http://www.wendangwang.com/doc/efe960bed681037ac6d62544G90 G91 G79 语法 G90 [G-codes] [operands ] G91 [G-codes] [operands ] G79 [G-codes] [operands ] 设置绝对编程，即，动作参考当前原点（到动作的位置）。 在增量系统内设置编程，即，动作参考之前动作到达的位置。 以归零点位置坐标为参考进行编程，只有在其编程的程序段中才有效。其中 G-codes operands 说明： 如果这些编码都没有被编程，默认编程模式是绝对的或说是 G90，即，坐标参考所定义的工作原点。 G90 和 G91 是模态的，而 G79 不是。在用 G79 执行完它所在的那一个程序段后，控制器会恢复之前程序段 的编程模式。 使用字符&gt;&gt;，在同一程序段中，可以混合增量/绝对两种编程模式。 字符&gt;&gt;置于一个数值之前，表示其必须被作为一个增量值，字符&gt;&gt;只有在 G90 绝对编程激活时才有意义，在 遇到想用 G91 的场合下，可以考虑选用此方法来代替。 示例： G90 G1 X   80 Y &gt;&gt;   35 Z-70 Y 轴是增量模式。 同 G90, G91 和 G79 兼容的其他 G 编码（见第一章“兼容的 G 编码”表）。 可以用在 G 字母程序段中的任一运算值或编码。45004457K90

Prima Electro S.p.A.Type of manual示例： 这个示例显示了如何使用不同的参考系统：绝对，增量和归零点位置。YAbsolute Origin 1&quot;HOME&quot; PositionHOMEMachine Zerox程序： (UGS,1,X,-50,100,Y,50,100) (UAO, 1) N1 G X Y N2 X30 Y40 N3 G91 X50 Y25 N4 X-71 Y12 N5 G90 X110 Y35 N6 G79 X70 Y55 ; 采用工作原点 1 ; X 和 Y 定位到工作原点 1（假设默认模式是 G90） ; X 和 Y 定位于点 1 ; 增量模式定位于点 2( X 50, Y 25 从点 1http://www.wendangwang.com/doc/efe960bed681037ac6d62544) ; 增量模式定位于点 3( X-71, Y 12 从点 2) ; 绝对模式定位于点 4 ( X 110, Y 35 从工作原点 1) ; 定位到点 5 (X 70, Y 55 从归零点位置)45004457K91

Prima Electro S.p.A.Type of manual3.50G92 G98 G99 – Axis PresettingG92 和 G98 是可以二者选其一的轴的新位置设定方法，它们在程序中要独占一行，新位置和旧位置分别存放 在不同的寄存器，所以刀补和其他工件原点不会因此而受到破坏，G99 则是取消这个新位置。 语法 G92 axes G98 axes其中： axes 说明： G98 和 G92 的差别仅在于 G98 可以用在镜像轴而 G92 则忽略镜像轴。 遇到以下该功能取消： G99 M2 M30 系统的复位 PLUS 当前的复位对 G92 和 G98 没任何影响，G92 和 G98 只是把当前位置视为所编程的位置，轴却不会产生移 动。 示例： ........ ........ G0 X100 Y80 G92 X0 Y0 ........ ........ 轴名称 （ 最多 6 个）Y80100X45004457K92

Prima Electro S.p.A.Type of manual3.51G04 G09 – 程序段尾部延时和减速有两个 G 编码属于这类： G04 G09 语法 G04 [G-codes] [operands ] G09 [G-codes] [operands ] 在程序段结束时作延时 在程序段结束时作减速其中： G-codes operands 说明： G04 在程序段动作结束时引起停顿。停顿时间由 DWT 定义（见后一节），所以 DWT 要在 G04 之前被赋值。 如果没有 DWT 被赋值，系统会采用默认值，只有当控制器在点对点（G29）中，G04 才被允许采用，且只有 在其编程的程序段中才有效。在 DWT 中设置的值可以以秒为单位(G94 或 G95 下且 G0 激活时)或以转http://www.wendangwang.com/doc/efe960bed681037ac6d62544数(G95) 为单位。 G09 强制进给率在其编程的程序段结束时为 0，但是不改变工序中轮廓的加工状态。G09 不会在控制器状态 中引起任何改变，且只有在其编程的程序段中有效。 其他与 G4 和 G9 兼容的 G 编码（见第一章“兼容的 G 编码”表）。 可以用在 G 字母程序段中的任一运算值或编码。V G4DWT VtG9t45004457K93

Prima Electro S.p.A.Type of manual3.52t - 程序段执行时间在 G93 和 G94 中，在程序段结尾处编写一个执行时间字母是可行的。 示例： G1 X10 Y1 t6 ；用 6 秒时间完成这一动作 说明： t 字母只在其编程的程序段中有效。时间以秒为单位，控制器自动计算进给率，在程序段中编程的轴动作将 按这个进给率执行。3.53DWT (TMR) – 停顿时间DWT 命令让你在程序段结束时分配一个停顿时间。这个停顿时间被 G04 和固定循环程序段使用。 尽管 DWT 命令可以在程序的任何地方编程，但是一定要在 G04 或固定循环之前。 语法 DWT = value其中 value 是时间，以秒或旋转为单位。其可以直接用一个十进制数编程或间接用 E 参数编程。 示例： DWT = 12.5 E32 = 13.4 DWT = E32 12.5 秒的停顿时间 分配值 13.4 给 E32 变量 分配一个 13.4 秒的停顿时间45004457K94

Prima Electro S.p.A.Type of manual3.54G93 – V/D 进给率G93 定义轴进给率（F）为执行该动作过程需要时间（分钟为单位）的倒数。 1 F = ----T 线性插补 Feedrate F = ------------Distance 圆弧插补 Feedrate F = -------------Arc 其中： Feedrate Distance Arc 线性或圆弧速度，以 mmpm(G71)或 ipm(G70)为单位 线性动作的向量距离，以英寸或毫米为单位http://www.wendangwang.com/doc/efe960bed681037ac6d62544弧形长度，以英寸或毫米为单位 F 字母在 G93 激活的程序段中是必需的。示例： G93 G1X. . Y. . F. . X. . Y. . F. .45004457K95

Prima Electro S.p.A.Type of manual3.55VFF - 前馈该命令启用 VFF/或者取消 VFF。 语法 VFF=value 其中： value 可以是： 0 取消 VFF：即允许跟随误差对实际加工影响存在。 1 启用 VFF 注意： VFF 在 AMP 中的默认值为 1。修改轴坐标参考系统的编码 这类中的命令能让你改变轮廓加工所在的笛卡尔参考系统。 命令 SCF MIR ROT UAO UTO UIO 作用 刻度比例因数 镜像加工 插补平面旋转 工作原点 临时原点 增量原点当激活时，坐标的改变要遵循以下的优先次序： SCF - G70/G71 - MIR - ROT - ORIGINS.45004457K96

Prima Electro S.p.A.Type of manual3.56SCF – 刻度比例因数SCF 命令为编程轴分配一个刻度比例因数，控制器应用这个刻度比例因数在 SCF 命令所指定的轴上，该轴的 刻度将会以该因数进行比例缩小或者放大。 语法 (SCF [axis1, . . . , axis9]) 或 (SCF [,value])其中： value 编程刻度比例因数。你可以直接用一个十进制数编程刻度比例因数或用一个 E 参数间接编程。 axis1 . . . axis9 说明： 你可以在 SCF 命令中指定至多 9 个轴。如果命令中只是提及刻度比例因数而没提及任何轴，则该比例应用于 所有轴；如果在命令中提及了部分的轴，那么没有提及的轴，将不会采用刻度比例缩放；如果 SCF 命令中没 有任何参数，则代表取消任何轴之前有或者本来就没有采用的刻度比例缩放。 示例： (SCF, 3) . . . SCF,X2.5,Y3)应用一个 2.5 的刻度比例因数到 X 轴，一个 3 的比例因数到 Y 轴，对于所有其他轴取消比例缩 放。 http://www.wendangwang.com/doc/efe960bed681037ac6d62544. . (SCF) 对所有轴取消比例缩放。 应用一个 3 的刻度比例因数到所有轴。 在系统中设置的名称。系统复位会使刻度比例因数对所有轴失效。45004457K97

Prima Electro S.p.A.Type of manual3.57MIR - 镜像加工MIR 命令是在当前参考轴下，对命令中指定的轴的方向进行反向，使得执行该命令后该轴运动方向和原来运 动方向成镜像对称。 语法 (MIR ,[axis1, . . . , axis9])其中： axis1. . .axis9 Is the name of the axis to be moved in mirror. 实行镜像的轴名。 说明： 在 MIR 命令中，你可以至多编程 9 个轴。每个 MIR 命令中，轴只能编程一次。没有在 MIR 中编程的轴，如果 之前采用了镜像功能将会被关闭。 如果在 MIR 命令中没有任何轴被指定，则所有轴都被取消镜像功能。 如果你一起使用平面旋转（ROT）和反向（MIR）命令，控制器会以下面的顺序处理：先 MIR 再 ROT。系统复位可使 MIR 命令在所有轴上失效，相当于一个没有任何参数的(MIR)。 例 1： 下面这些示例显示了镜像加工是如何工作的。Y (MIR,X) (MIR) 4 4 3321 012 X21123 (MIR,X,Y)44 (MIR,Y)3. . N24 (MIR,X) . . .镜像未激活时在第一个象限发生的动作是参考当前坐标系统的。 此时镜像加工对 X 轴生效。编程 X 动作却生成一个在第二个象限内显示的动作。45004457K98

Prima Electro S.p.A.Type of manualN42 (MIR, X, Y) . . .镜像加工对 X 和 Y 轴生效。编程动作结果在第三个象限内显示。N84 (MIR, Y) 镜像加工对 Y 轴激活，但取消了 X 轴的镜像，因为 MIR 命令中 X 轴未被提及，之前的镜像加 工被取消。产生的效果在第四个象限内显示。 .http://www.wendangwang.com/doc/efe960bed681037ac6d62544 . . N99 (MIR) 例 2： 这个示例显示了如何使用 MIR 命令。同时也请注意 RPT 和 ERP 的使用。 镜像加工对所有的轴都未生效，恢复到在第一个象限内的动作。90404090程序： (UGS, X, -100, 100, Y, 0, 80) N199 (DIS.&quot;MILLING CUTTER D =16&quot;) N200 S1500 T8.8 M6 N201 N202 N203 N204 N205 N206 N207 N208 N209 (RPT, 2) G X90 Y20 M3 Z-100 G1 Z-105 F150 X40 F200 G2 Y60 I40 J40 G1 X90 G Z-100 (MIR, X) ；重复执行两遍N210 (ERP) N211 (MIR) N212 Z；重复语句的结束位置45004457K99

Prima Electro S.p.A.Type of manual3.58ROT (URT) – 插补平面旋转ROT 通过编程一个角度值来旋转当前的插补平面。旋转中心是当前工作原点。 语法 (ROT, angle)其中： angle 表示角度值，以十进制度为单位。你可以直接用一个十进制值编程这个角度，或用一个 E 参数间接编 程。正角度逆时针方向移动当前插补平面的横坐标轴。负角度时是顺时针移动。如果角度为 0，平面旋转取 消。 说明： 注意归零点（G79）的机器坐标不可能被旋转。 如果你一起使用轴旋转(ROT)和反向（MIR），控制器以下面的顺优先次序执行他们：首先 MIR，然后 ROT。 系统复位会取消平面旋转。其等同于编程（ROT,0）。模式 0 （不指定模式则默认是 0） 的例子：Y(UAO, 1) (ROT, 30) (UIO, X100, Y50)3050100X模式 1 的例子：Y(UAO, 1) (ROT, 30, 1) (UIO, X100, Y50)30 100 X45004457K50100

Prima Electro S.http://www.wendangwang.com/doc/efe960bed681037ac6d62544p.A.Type of manual例 1：Y3050100X程序： (UTO, 1, X100, Y50) (ROT, 30) . . (UAO, 1) (ROT, 0) 例 2：Y 70 25激活工作原点 1 且同时应用临时原点（补偿值）X100 和 Y50参考临时原点指定逆时针方向 30 度旋转 程序这个部分的动作是以临时原点为擦参考，逆时针 30 度方向旋转。 重新激活绝对工作原点 1 指定一个 0 度旋转取消平面旋转。25102055402230X程序： N99 (DIS, &quot;DRILLING D=6&quot;) N100 S2000 F200 T3. 03 M6 N101 (UTO , 1, X30, Y22) N102 (ROT, 20) N103 G81 R-90 Z-110 M3 N104 X25 Y25 N105 X40 Y10 N106 X55 N107 X70 Y25 N108 G80 Z N109 (UAO, 1) N110 (ROT, 0) N111 S1000 T4.4 M645004457K101

Prima Electro S.p.A.Type of manual例 3： 这个示例显示了如何结合重复语句（RPT）和变量一起编程平面旋转(ROT)功能。程序： N148 N149 N150 N151 N152 N153 N154 N155 N156 N157 N158 N159 N160 N161 N162 (DIS, &quot; ...&quot;) S1500 T5.5 M6 E25 =0 (RPT, 8) ( ROT, E25) G X40 Y M3 Z0 G29 G1 Z-10 F150 X80 F200 Z-18 F150 X40 G Z0 E25 =E25   45 (ERP) (ROT, 0)45004457K102

Prima Electro S.p.A.Type of manual3.59UAO – 使用工作原点UAO 命令让你激活http://www.wendangwang.com/doc/efe960bed681037ac6d62544并使用存储在内存中的工作原点之一。 语法 (UAO, n [,axis1, . . . , axis9])其中： n 标。 axis1,...,axis9 是工作原点 n 的轴名称。 说明： UAO 命令允许多达 9 个轴。 在 UAO 命令中，如果只是指定了工作原点号而没有指定轴名称时，则当前工作原点对应的各轴原点应用到各 个轴。在重启或者系统复位的情况下，或者 n=0 且没有轴指定时，所有的轴参考归零点位置。 如果程序对每个轴要求单独的工作原点，对每个需求的轴分别编程一个 UAO 命令。 原点值自动转换并以当前单位模式(G70/G71)显示。 示例： (UAO,1) . . (UAO, 2, X, Y) (UAO, 3, Z) . . 点 1。 (UAO, 1) . . . (UAO, 0) 对所有轴重新激活原点 1。 对所有轴激活工作原点 1。 定义工作原点号。其可以是在 0 和 10 之间的一个整数或一个 E 参数。0 代表启用机器归零点位置坐只对 X 和 Y 轴激活工作原点 2。 对 Z 轴激活原点 3。 程序的这个部分对 X 和 Y 轴使用原点 2，对 Z 轴使用原点 3，对所有其他的轴使用原对所有轴重新激活归零点位置。45004457K103

Prima Electro S.p.A.Type of manual3.60UTO (UOT) – 使用临时原点UTO 命令对每个轴的指定工作原点位置临时增加一个编程量。 语法 (UTO, n ,axis1 [,axis2, . . . , axis9])其中： n 定义将要被临时修改的工作原点代号。其是从 0 到 10 的一个整数。如果 n=0，编程的增加量加到归零点位 置值基础上。 axis1,...axis9 是一个轴名称和一个增加量。控制器将这个增加量作为一个补偿值，将其加到那个轴的工作原 点值上。 说明： 在 UTO 命令中，你必须至少指定一个带增加量的轴，但至多可以指定 9 个带增加量的轴。 在 UTO 命令中的轴范围必须以当前的测量单位(G70/ G71)编程。 如果在 UTO 程序段中，一个轴被省略，那个轴的当前工作原点仍保http://www.wendangwang.com/doc/efe960bed681037ac6d62544持。 一旦你激活一个临时原点，其会保持激活直到你： 用UTO命令激活一个新的临时原点 用UAO命令激活一个工作原点 执行控制器重启 如果一个刻度比例因数(SCF)被设置，控制器将其应用到 UTO 临时原点中。 例 1： 增加量可以是在下面程序段中显示的 E 参数： (UTO,1,XE100)45004457K104

Prima Electro S.p.A.Type of manual例 2：Y 100YN20 X N10 Y 25001 X YN30X5002 N40 X程序： N10 (UAO,1) . . . N20 (UTO, 1, X100, Y100) . . N30 (UTO, 2, X-250, Y50) . 对所有轴激活工作原点 1。 在程序的这个部分，所有轴使用工作原点 1。 应用一个临时原点（补偿值）到原点 1，X100 和 Y100。 在程序的这个部分，轴使用原点 1，X100，Y200 作为临时原点。 激活工作原点 2 并且将临时原点（补偿值）加到工作原点 2。 程序的这个部分使用工作原点 2，并添加 X250 和 Y50 作为补偿值，其他轴使用工作原点 1。 N40 (UAO, 2) 对所有轴重新使用工作原点 2。45004457K100105

Prima Electro S.p.A.Type of manual3.61UIO – Using Incremental Origin与 UTO 极为类似，区别是 UIO 仅对当前工作原点添加一个编程增加量，也就是补偿值。 语法 (UIO, axis1 [,axis2, . . . , axis9])其中： axis1,...axis9 是一个轴名称和一个增量值。控制器将这个增量值作为一个补偿值，并将其加到那个轴的当前 工作原点值上。 说明： 你必须在 UIO 命令中至少指定一个轴，但你至多可指定 9 个轴。在每个 UIO 命令中，一个轴只可以被指定一 次。 在 UIO 命令中的轴增加量必须以当前的测量单位(G70/ G71)编程。 如果在 UIO 程序段http://www.wendangwang.com/doc/efe960bed681037ac6d62544中，一个轴被省略，那个轴的当前工作原点保持。 一旦你为一个轴激活一个原点增量，其会保持激活直到你： 用UIO命令为轴激活一个新的原点增量 用UAO命令激活一个工作原点 执行控制器重启 如果一个刻度比例因数(SCF)被设置，控制器将其应用到 UIO 增量原点中。 示例：程序： N12 (UAO,1) 对所有轴激活工作原点 1。 N65 (UIO, X20, Y20) N121 (UIO, Y-40) N180 (UIO, X-45) N230 (UIO, Y35) 从原点 1 应用一个 X20 和 Y20 的增量补偿值。对其他轴保持归零点坐标系有效。 再应用一个 Y-40 增量补偿值给 Y 轴。X20 增量原点保持有效。 再应用一个 X-45 增量到 X 轴。 再应用一个 Y35 增量 Y 轴。45004457K106

Prima Electro S.p.A.Type of manualN300 (UAO,1) 对所有轴恢复工作原点 1。45004457K107

Prima Electro S.p.A.Type of manual超行程和保护区域设定在这类中的命令定义超程限制和受保护的区域，描述如下： 命令 SOL DPA PAE PAD 功能 定义软超行程位置 定义受保护区域 激活一个受保护区域 取消一个受保护区域45004457K108

Prima Electro S.p.A.Type of manual3.62SOL (DLO) - 软超行程SOL 命令定义从当前原点坐标系测量的轴行程范围。 语法 (SOL,axis-name,lower-limit,upper-limit)其中： axis-name lower-limit upper-limit 说明： 如果所定义的行程范围还大于 AMP 里面所设定的行程范围，则会报错。 当你编程 SOL 命令时，测量单位基于 G70/G71。刻度比例因数（SCF）应用于该行程范围。 所要限制的行程范围的轴名称。 下极限位置 上极限位置，数值必须大于下极限示例：Y2http://www.wendangwang.com/doc/efe960bed681037ac6d62544000 X 200300程序： (SOL, X, -300, 300) . . . (SOL, Y, -200, 200)45004457K3000109

Prima Electro S.p.A.Type of manual3.63DPA (DSA) – 定义保护区域DPA 命令定义一个受保护区域。 语法 (DPA, n,axis-name1,lower-limit1,upper-limit1,axis-name2,lower-limit2,upper-limit2 )其中： n axis-name1 是区域标识符（1-3）。 是横坐标名。lower-limit1 是横坐标下限。 upper-limit1 是横坐标上限。 axis-name2 是纵坐标名。 lower-limit2 是纵坐标下限。 upper-limit2 是纵坐标上限。 说明： 在开始一个线性或圆弧插补的动作之前，控制器会检查这个动作是否进入一个“受保护区域”。 在一个程序中，你可以为机床定义至多 3 个受保护区域，每个区域参考当前的原点坐标系。 示例：Y area 1 area 2 100 50 0 0 50 100 X200300100编程： N1 (DPA,1, X, -300, -100, Y, -100, 100) N2 ( DPA, 2, X, 200, 450, Y, -50, 50) N3 (PAE, 1) N4 (PAE, 2) N5 T1.1 M6 . . . N80 (PAD, 1) . . .45004457K4500110

Prima Electro S.p.A.Type of manualN99 M303.64PAE (ASC) – 激活保护区域PAE 命令激活受保护区域。 语法 (PAE, n) 其中： n 是受保护区域标识符，也就是其代号，由之前的 DPA 命令定义（范围是 1-3）。示例： (PAE,2) 激活受保护区域 2，使其生效。3.65PAD (DSC) – 取消受保护区域控制http://www.wendangwang.com/doc/efe960bed681037ac6d62544PAD 命令使受保护区域控制失效。 语法 (PAD, n)其中： n 是将被取消的受保护区域标识符，也就是其代号（范围是 1-3）。示例： (PAD,3) 取消受保护区域 345004457K111

Prima Electro S.p.A.Type of manual3.66虚拟轴应用虚拟轴提供一系列功能使实际坐标系通过旋转和平移方式虚拟成为三维空间上的虚拟坐标系，是一种假象的 坐标系，实际坐标系并未改变。3.66.1Virtual AxesVirtual axes are declared in the configuration but are not associated to any physical parameter (for further information, refer to the AMP Manual). Virtual axes are used: to handle planes rotated in space when cartesian planes are transformed into planes measured in polar coordinates when cartesian planes are transformed into planes measured in cylindric coordinates to perform moves in the tool direction to perform tool length compensation during the execution of profiles with five simultaneous axes, such as a tool mounted on a wrist with two degrees of freedom. Prior to performing circular moves (G02-G03) on a programmed virtual plane you must define the interpolation plane withttp://www.wendangwang.com/doc/efe960bed681037ac6d62544h the G16 code. When virtual axes are disabled the system forces the default plane configured in AMP as interpolation plane. Virtual axes are disabled by a system reset.3.66.2COMMAND UPR UVP UVC TCPVirtual modes available on 10 Series CNCFUNCTION (USE PLANE ROTATED) Rotation of cartesian axes XY and Z in space. (USE VIRTUAL POLAR) Machining transformations from cartesian coordinates to polar coordinates (USE VIRTUAL CYLINDRICAL) Machining transformations from cartesian coordinates to cylindrical coordinates. (TOOL CENTER POINT) Programming in part ranges rather than in machine ranges.45004457K112

Prima Electro S.p.A.Type of manual3.67UPR - Rotation of Cartesian axesUPR (USE PLANE ROTATED) allows definition of a system of three virtual axes translated and rotated. 语法 (UPR,type, af1af2af3, av1av2av3[rot1,rot2,rot3 [,q1,q2,q3 [,hor,ver]]]) (upr,type, af1af2af3, av1av2av3[rot1,rot2,rot3 [,q1,q2,q3 [,hor,vhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544er]]]) (UPR) (UPR,99) (UPR, 5, af1af2af3, av1av2av3, type_req, pos-xx-H, pos-xx-V, n, ref-pos-xx-H, ref-pos-xx-V)其中： typeSpecifies the rotation mode: 0= absolute rotation angles are referenced to physical axes 1= incremental rotation angles are referenced to the system of axes used for incremental programming. This type of rotation is possible if a previous rotation has been programmed (absolute the first time, incremental for subsequent times.) 2= absolute, with transformation on 5 axes The characteristics are similar to those of type 0 but the rotation of the linear axes influences the position of the two rotating axes. Upon activation of the UPR function, the rotating axes take on a new value which identifies the position of the tool axes with respect to the virtual system. 3= incremental, with transformation on 5 axes The characteristics are similar to those of type 1 and also encompasses the points outlined in the previoushttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 item. 4 = rotating plane automatically determined according to the direction of the tool axis. 5 = does not define a new virtualisation: it enables you to request the physical or virtual positions of the rotary axes relative to the currently active virtualisation. 6 = as 4 but with 5-axis transformation (see 2). 8 = rotating plane automatically determined according to the orizontal rotary axis positon. It’s like 4 but without considering the rotary vertical axis 10 = global, type 0 The characteristics are similar to those of type 0, but the programmed rotation remains active even with subsequent non global UPR’s.45004457K113

Prima Electro S.p.A.Type of manual 12 = global, type 2 The characteristics are similar to those of type 2, but the programmed rotation remains active even with subsequent non global UPR’s. 14 = global, type 4 The characteristics are similar to those of type 4, but the programmed rotationhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 remains active even with subsequent non global UPR’s. 16 = global, type 6 The characteristics are similar to those of type 6, but the programmed rotation remains active even with subsequent non global UPR’s. 18 = global, type 8 The characteristics are similar to those of type 8, but the programmed rotation remains active even with subsequent non global UPR’s. 99 without any further parameter, disables all active UPR modes, including global rototranslation. Names of the three physical axes to be handled in virtual mode (e. g. XYZ). Names of the three virtual axes to be moved (e. g. UVW). Rotation angles expressed in degrees. Direction is selected with the right hand rule, which is discussed in the next section. These parameters allow the origin of the reference system to determine the origin of the reference system:    af1af2af3 av1av2av3 rot1,rot2,rot3 q1,q2,q3  In an absolute rotation, q1, q2 and q3 are the co-ordinathttp://www.wendangwang.com/doc/efe960bed681037ac6d62544es of the system origin. They are relative to the origin that was active when UPR was programmed.   In an incremental rotation, q1, q2 and q3 are the increments applied to the current origin. The new system origin is the result of adding these increments to the co-ordinates of the current one. If q1,q2,q3 are not present, the origin of the reference system coincides with the origin of the physical system being used. hor,ver Values in degrees of angles interior to the round angle (between -360&#176; and  360&#176;) identifying the origin of the horizontal and vertical rotary axes. This must always be regarded as translations of the physical axes. Type of position requested of the system:   0 = physical position pos-xx-H   1 = virtual position Angle expressed in degrees; this is the physical or virtual position of the horizontal rotary axis to which the rotation matrices must be applied in order to determine the corresponding positiohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544n requested. Angle expressed in degrees; this is the physical or virtual position of the vertical rotary axis to which the rotation matrices must be applied in order to determine the corresponding position requested. E variable indicator to be used as a starting point to save the values of the requested angles as returned by the system: the first pair (horizontal axis position, vertical axis position) corresponds to the solution closest to the ref-pos-xx angles, the second pair (Hor, Ver) is complementary to the first. Angle expressed in degrees; it is the value around which the solution for the horizontal axis must be determined.Type_reqpos-xx-Vnref-pos-xx-H45004457K114

Prima Electro S.p.A.Type of manualref-pos-xx-V no parameterslower case programming (UPR)WARNINGAngle expressed in degrees; it is the value around which the solution for the vertical axis must be determined. (UPR) without parameterhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544s disables the UPR mode, leaving the global mode only, if present. If no global rotation has been programmed, commands (UPR) and (UPR,99) are equivalent. If the three-letter block is programmed in lower case, the angles and/or origins can be disabled using the UPR algorithm without exiting from the &quot;CONTINUOUS MOVEMENT&quot; mode. The lower case three-letter block (upr,...... must only be used to alter the parameters of the (UPR, ...) programmed in advance. The axis sequence cannot be altered. A global type rotation cannot be programmed. In a 5-axis transformation, the behaviour of the lower case upr may, in some instances, differ from that of the upper case UPR. Since in continuous mode synchronisation with the physical positions is not applicable, the values of the angles determined by the system have been normalised relative to 0.0 and therefore might turn out to be complementary to the desired values. At any rate, the soluhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544tions provided for the tool position retain their validity.ATTENZIONE45004457K115

Prima Electro S.p.A.Type of manualTo select the direction of rotation of the system of virtual axes you must apply the right hand rule. Y v  Z  w u XRight hand rule 说明： UPR allows programming of any machine function in a space that has been rotated by the specified angle with respect to the machine tool Cartesian system. This lets you program the profile in the normal Cartesian space (XYZ) and then have 10 Series recalculate the axes moves according to the virtual planes resulting from rotation. By programming a global UPR you can apply an initial rototranslation to serve as a term of reference for all subsequent UPR’s. This makes it possible to perform the same part program, which, in its turn, may contain other geometric transformation instructions, even when the part to be processed is, for instance, fastened to the http://www.wendangwang.com/doc/efe960bed681037ac6d62544bench by brackets set along different directions. The activation of a global type UPR is not rated as a previous UPR for purposes of incremental or lowercase programming. The activation of a global type UPR cancels any previous virtualisation, resulting in the reset of any displacements. When a UPR type 2, 3, 4, 6 or 8 is used, or any of the corresponding global type UPR’s are used, the system needs the machine characteristics, which must be entered in the TCP table according to the rules established by the TCP itself. This feature is separate form TCP, or rather, it can work whether TCP is active or not. When UPR and (TCP, 5) are active simultaneously, the movement of the axes will influence the movement of the virtual axes. With modes 2 and 3, the tool axis, once identified by the programming of the rotating axes, takes on the same position within the virtual reference system as it has in the reference system identified by the Cahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544rtesian system.45004457K116

Prima Electro S.p.A.Type of manualModes 4, 6 and 8 and the corresponding global type modes determine the new rotation plane based on tool direction (i.e. based on the positions of the rotary axes); mode 8 is only based on the orizontal rotary axis. On the new plane, supposing the programming UPR, 4, XYZ, UVW ..., the W axis will coincide with the direction of the tool, the U axis will lie on the original XY plane and, consequently, the V axis will be based on the rule that determines the Cartesian axes. A type UAO or UTO origin cannot be programmed with an active virtualisation. Origins on rotary axes implemented with a UIO command are not managed.ZV WYUXBy means of angles rot1, rot2 and rot3, the UVW axes determined in this way may be further rotated; an increase (see type 1 or 3) will be applied to the new axes. The RESET command disables the UPR mode. When a global UPR ihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544s programmed, the values of rot1, rot2, rot3 must be IMPORTANT between –90&#176; and  90&#176;. For angles outside this range, when passing from one virtualisation to another, the algorithm generating the rotary axis position could generate unwanted rotations (unwanted, but still congruent with the position of the tool). The UPR is insensitive to the DAN: the axes to be specified in the UPR IMPORTANT are the names of the physical and virtual axes desired, regardless of any DAN commands executed previously.IMPORTANTThe UPR 8 manual move allows a realtime rotation of the tern at the same time of the orizontal rotary axis rotation. Therefore, a move on the virtual axis (i.e. U) contemporary to the rotary axis, makes the resulting move as an arc instead of a linear move.45004457K117

Prima Electro S.p.A.Type of manualIMPORTANTStarting with release 7.4 in order to remedy operating anomalies and solve solution ihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ndeterminacy problems during a virtualisation involving a 5-axis transformation, the algorithms employed to determine the positions of rotary axes have been changed. Downward compatibility is ensured by defining the !R73MODE user variable. !R73MODE = 1 : the calculation of the virtualisation is by means of the old algorithms, in line with release 7.3 !R73MODE = 0 or not defined : the calculation of the virtualisation is by means of the new algorithms as are used in release 7.4 or higher This user variable is read solely in conjunction with upper case UPR programming. A programming error is notified if the rotary axes origins are programmed in the three-letter UPR code and one of the following conditions occurs: - user variable !R73MODE is set on 1. This is so because the aforementioned programming has been managed starting with release 7.5 and conflicts with the use of the calculation algorithms associated with release 7.3. - the thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ype of UPR programmed does not require a 5-axis transformation.IMPORTANTERotation modes: The three-axis cartesian system rotates sequentially by the programmed angles. This means that: A) The af1 af2 af3 system of coordinates rotates by a rot1 angle around the af1 axis B) The new av1' av2' av3' system of coordinates, which results from the above described rotation, rotates by a rot2 angle around the av2' axis C) The av1&quot; av2&quot; av3&quot; system of coordinates, which results from the rotations described in A) and B), rotates by a rot3 angle around the av3' axis After these three operations have been completed, the virtual axes of the resulting system will be av1 av2 av3. Since steps A) B) and C) are carried out sequentially, the order in which angles and axes are programmed in the block is critical.IMPORTANT45004457K118

Prima Electro S.p.A.Type of manual  Using UPR In the following examples it is suhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544pposed that the the three-axis cartesian system XYZ is the reference system. In the examples 1, 2, 3, 4, 5 the reference system origin coincides with the origin in use at the time of programming UPR. Example 1: . . GXYZ (UPR,0,XYZ,UVW,30,45,60) G1F5400 U100.4V9.12 W-70 . U70.345 W-20 . . . . . G16UV G02 U100 V70 R15 G1 U120 W10 . . (UPR) X1 Z4.9 . Example 2: . . . GXYZ20 (UPR,0,XYZ,UVW,10,0,80) G1F4000 U50 V70 . U90 V80 W60 . . (UPR) . . . The UVW system may be obtained by: A) rotating the XYZ system by 10 degrees around the X axis. B) rotating the U'V'W' system resulting from A) by 80 degrees around the W' axis The UVW system may be obtained by: A) rotating by 30 degrees the XYZ system around the X axis B) rotating the U'V'W' system resulting from A) by 45 degrees around V' C) rotating the U''V''W'' resulting from A) and B) by 60 degrees around W''45004457K119

Prima Electro S.p.A.Type of manualExample 3: . . .http://www.wendangwang.com/doc/efe960bed681037ac6d62544 GXYZ20 (UPR,0,ZYX,ABC,80,0,10) G1F3000 A50 B70 . A90 B80 C60 . . (UPR) . . The UVW virtual system discussed in Example 2) is different from the ABC system in Example 3). The ABC system may be obtained by: A) rotating the XYZ system by 80 degrees around the Z axis B) A) rotating the A'B'C' system resulting from by 10 degrees around the C' axisIMPORTANTExample 4: . . . (UPR,0,ZYX,WVU,0,50,60) U90V30 W10 . . . . (UPR) . . . The WVU system may be obtained by: A) rotating the XYZ system by 50 degrees around the Y axis. B) A) rotating the W'V'U' system resulting from by 60 degrees around the U' axis45004457K120

.

[此处图片未下载成功]

(UPR,0,XYZ,UVW,30,0,0) G16 UV

F1000 U50 V0 V30 .

.

[此处图片未下载成功]

U25 V35

(UPR,1,XYZ,UVW,60,0,0) U30 V20 . .

(UPR) GX10 Y25 . .

6:

.

[此处图片未下载成功]

GXYZ

(UPR,0,XYZ,UVW,30,45http://www.wendangwang.com/doc/efe960bed681037ac6d62544,60,10.8,20,-30.2) G1 F5400

.4V9.12W-70 U70.345 W-20 . . .

UV

U100 V70 R15 G1 U120 W10 . . (UPR) X1 Z4.9 .

.

[此处图片未下载成功]

. GXYZ

(UPR,0,XYZ,UVW,30,45,60,10.8,20,-30.2) G1F500

.4 V9.12 W-70 U70.345 W-20 . . . .

[此处图片未下载成功]

.

.

(UPR,1,XYZ,UVW,10,0,0,3,8,5) U120 V30 . .

.

(UPR)

.5 Y10 Z25 . .

8:

this case, we want to apply an initial rotation, say of 90&#176; around the Z axis, to the part program discussed in example 2:  .

[此处图片未下载成功]

. GXYZ

(UPR,10,XYZ,UVW,0,0,90) (UPR,0,XYZ,UVW,10,0,80) G1F4000 U50 V70 U90

W60 . .

(UPR,99)

Utilisation of type 5 upr.

us assume we are applying to a Double Twist type machine tool a virtualisation involving a 90&#176; rotation around the Z axis.

the sakehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 of brevity, let us denote with B the horizontal rotation axis, with A the vertical rotation axis, with WRK the corresponding virtual positions and with ABS the corresponding physical positions.

[此处图片未下载成功]

XYZAB

(UPR,2,XYZ,UVW,0,0,90)

you want the system to determine the physical positions corresponding to virtual positions A=0 and B=0,

[此处图片未下载成功]

with the solutions in the E variables being entered starting from indicator 10, program the following upr:

(UPR,5,XYZ,UVW,0,0,0,10,0,0)

UVP - Programming polar coordinates

permits to program axes moves with virtual coordinates. 语法

(UVP,af1af2,av1av2,r) (UVP) 其中： af1   af2   av1   av2   r   no parameters

linear axis (for example, X) physical rotary axis (for example, C) virtual abscissa axis (for example, u) virtual ordinate axis (for example, v)

http://www.wendangwang.com/doc/efe960bed681037ac6d62544radius the tool path must not enter  disable UVP by programming (UVP) without parameters

说明：

virtual mode permits to move an X linear axis and a C rotary axis by programming their coordinates in a UV cartesian plan. The (U,V) coordinates of any point on the virtual plane are translated into the (X,C) coordinates of the physical axis.

[此处图片未下载成功]

is requested to exceed the rapid feed, the r

minimum radius should be calculated using the following formula:

其中：

= minimum radius F = programmed feed (mm/min or inch/min) Vmax = rotary axis rapid speed

to the r parameter is attributed a negative value, the feed limitation is executed dinamically, in such a way to allow high feeds in working point that are quite far from the working centre.

[此处图片未下载成功]

Accelerations are calculated in a dynamic http://www.wendangwang.com/doc/efe960bed681037ac6d62544mode, therefore it is preferable to use this (r-) programming only when positioned at a certain distance from the working centre as, in this case, the rotary axis might be subject to too high accelerations

[此处图片未下载成功]

Programming examples with polar coordinates Example 1:

=110*180/(3.14159*800) T1.1M6 S1000M3 GC0X50Y0

(UVP,XC,UV,E0) G16 UV

G42U20VF110 V20 r3 U-15 b5 V-20 r5 U0

G2U20V0I20J-20 (UVP) GX50

[此处图片未下载成功]

2: T1.1M6

M3F300 GC0X80Y0-Z-5 (UVP,XC,UV,10) G16UV p1=U20V0 l1=p1,a90 c1=I0J35r-25 I2=U-15V0,a90 l3=U0V-20,a0 c2=I25J-30r-25 G21G42p1 l1 r3 c1 r4 l2 r5 l3 r3 c2 r3 l1 p1

G40 (UVP) GX80

[此处图片未下载成功]

_pol1.drw

UVC - Programming cylindrical coordinates

UVC command (USE VIRTUAL CYLINDRICAL) permits to program cylinhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544drical coordinates. 语法

(UVC,af1,av1,r) (UVC)

其中：

physical rotary axis (for example, B) av1 virtual axis (for example, W) r cylindrical radius on which the profile is executed no parameters without parameters disables UVC mode. 说明：

mode permits to move a Y linear axis and a B rotary axis by programming their coordinates on a WY plane. While the moves of virtual Y coincide with those of physical Y, each move of W corresponds to a circle arc, which is a function of the cylinder radius and must be translated into an angular move of the

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

B physical axis.

with cylindrical coordinates

[此处图片未下载成功]

[此处图片未下载成功]

l2=c1,c2

=I180J35r-25 l3=c2,c3 c4=c3,l1,r15 G21G41p1 Z-12 l1 c1http://www.wendangwang.com/doc/efe960bed681037ac6d62544 l2 c2 l3 c3 c4 l1

G40p2 GZ20 (UVC) M30

UVA -   Programming non orthogonal axes

UVA (USE VIRTUAL ANGULAR) command makes it possible to program non orthogonal axes by treating them as if they were orthogonal. 语法

(UVA,af1af2,av1av2,a) (UVA)   其中： af1 af2 av1  av2  a

parameters

说明：

type of virtualisation is used when you want to move two linear X Y axes that are not mutually orthogonal by programming the coordinates on a virtual orthogonal UV plane. The U axis, the abscissa of the new pair of axes, will be coaxial with axis X, whereas axis V will be perpendicular to U, forming an angle of 90&#176;- with axis Y.

origin of UV will coincide with the origin of XY. The position of a generic point P with coordinates (U,V) in the virtual plane is translated into the (X,Y) coordinates of the physical axes. While the movements of U coincide with those of thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e corresponding physical axis (X), every movement of V is translated into an interpolated movement of X and Y.

[此处图片未下载成功]

is the name of the first physical linear axis (e.g. X) is the name of the second physical linear axis (e.g. Y) is the name of the virtual abscissa axis (e.g. U) is the name of the virtual ordinate axis (e.g. V)

the angle, in degrees, subtended by two positive semi-axes of the physical linear axes

(UVA) without parameters disables the UVA mode.

of the XY plane and the corresponding UV plane

sign of parameter a is positive if the X axis, as it reaches its position

the Y axis, rotates around itself in the counterclockwise direction; it is negative if the direction of rotation is clockwise (in the example shown in the figure below, a is positive).

of a of 0&#176; and 180&#176; are not permissible, as this would entail two

http://www.wendangwang.com/doc/efe960bed681037ac6d62544physical axes arranged parallel to one another.

[此处图片未下载成功]

[此处图片未下载成功]

Example of programming with polar coordinates Example 1: N1 T1.1M6 N2 S1000M3

GX0Y0

(UVA,XY,UV,45)

G1U20VF110 N6 V30 N7 U0

V0 N9 U-10V10

(UVA) N11 GX50

[此处图片未下载成功]

TCP -  双摆头TCP

这个功能使得5轴机器（3个直线轴 2个旋转轴）的加工程序参考刀尖位置而并非旋转轴中心。

系统控制刀尖位置需要知道关于旋转轴的位置和双摆头的几何尺寸。 TCP算法启用可以通过在加工程序中添入TCP类的三字码指令。  复位或者编写（TCP）则取消该功能。

小写的（tcp，n）会修改某些参数但不会退出TCP功能和退出连续运动模式。

小写的（tcp，n）一定是用来修改此前编写的（TCP，n）的参数，而且数字n也必须保持和前面相同，另外，（tcp，n）中的n不能是5。 (tcp,[n]) 其中： n

补偿模式种类，它们会在后续的内容中提及。 说明：

在TCP程序段中你还必须写当前刀的信息，系统可以同时管理多达4个装在同一个双摆头上的不同刀具。 参数的设置必须依据图2.1所示的摆放角度和位置，这些参数被包含在User Table（用户表格）里面，有三种方式你可以修改它们：1.表格编辑器2.特定的PLC函数3.加工程序中的L变量。你还可以用USER TABLE EDITOR(用户表格编辑器)的SETUP utility上传之前已经设置好的配置文件 注意：

关于PLC函数的参数修改方式请参考PLUS Library http://www.wendangwang.com/doc/efe960bed681037ac6d62544Manual手册中关于$TBLPUTD 和 $TBLGETD函数使用方法的介绍。

从表格编辑器访问User Table（用户表格）请参考User Manual手册。

[此处图片未下载成功]

TCP 关于双摆头机器的参数表格

[此处图片未下载成功]

Prima Electro S.p.A.

of manual

水平旋转平面补 偿

98 - L388 Var 1

is the offset --expressed in degrees-- to be applied to the horizontal head axis so that the plane that supports the tool coincides with the YZ plane of the machine.它是一个补偿值，单位是 角度， To calculate this offset value, rotate the horizontal axis until the plane that supports the tool coincides with the YZ plane of the machine, and then direct the vertical head towards Y- with a positive head move. Then pick up the displayed coordinate, multiply it by the rotation coefficient of the horizontal head (Horizontal head rotation coefficient) and change the sign of the result.

, 2, 3, 4, 5

水平旋转轴方向

98 - L389 Var 2

从上往下俯视，按http://www.wendangwang.com/doc/efe960bed681037ac6d62544以下设置：  1 顺时针方向 - 1 逆时针方向

(图 2.3)

, 2, 3, 4, 5 1, 2, 3, 4, 5

垂直旋转轴方向

98 - L390 Var 3

从左往右俯视，按以下设置：  1 顺时针方向 - 1 逆时针方向

(图 2.2)

alterable in continuous through lower case programming (tcp,n).

K

[此处图片未下载成功]

TCP 表格(接上)

[此处图片未下载成功]

alterable in continuous through lower case programming (tcp,n).

双摆头上刀夹 1

[此处图片未下载成功]

[此处图片未下载成功]

Tool holder 2

Tool holder 3

[此处图片未下载成功]

[此处图片未下载成功]

下面是分别从机器前端，机器顶部俯视和从机器侧面角度得到的三个图形：

[此处图片未下载成功]

图

[此处图片未下载成功]

2.1

图2.2

图2.3

[此处图片未下载成功]

动态设定

[此处图片未下载成功]

[此处图片未下载成功]

Prima Electro S.p.A.

of manual

mode 插补模式

91 - Var http://www.wendangwang.com/doc/efe960bed681037ac6d625443

whether or not the rotary axes are interpolated in conjunction with the linear axes. If not interpolated, the rotary axes follow the linear axes moves. Allowed values are: 0 - Rotary axes interpolated in conjunction with linear axes 1 - Rotary axes follow linear axes Select mode 1 if the velocity on the profile should not be affected by rotary axes motion. Specifies whether the rotary axes must be interpolated only by the error or must be treated as linear axes. Allowed values are: 0 - Rotary axes interpolated as linear axes 1 - Rotary axes interpolated only by the error. With interpolation mode 1, this parameter defines whether acceleration/deceleration ramps will be used for rotary axes or whether velocities proportional to the linear axes moves will be used. Allowed values are as follows: 0 - No ramps 1 - Ramps If 1 is selected, the velocity diagram will be calculated using the configured parameterhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544s for rotary axes, irrespective of linear axes moves.

2 3 5

type 插补形式

91 - Var 4

2 3 5

插补器

92 - Var 1

2 3 5

K

[此处图片未下载成功]

动态模式 (接上)

[此处图片未下载成功]

以上数据全部是以毫米为单位。

The following figures illustrate significance of the TCP parameters used for management of spherical and 平头刀尖s; the abbreviation U.T. indicates the corresponding number in the User Table.

[此处图片未下载成功]

图 2.5 平头刀尖

[此处图片未下载成功]

图 2.6 平头刀尖

模式 1 (TCP,1)

在(TCP,1)中，坐标参考的是工件，当加工程序编程了直线轴和旋转轴移动，刀具是极力地去贴着工件表面，加工程序中所编写的直线视为是工件上的路径。

旋转轴是在迎合直线轴确定的空间路径时使得刀尖按照编程的角度贴着该轮廓表面，因此达到这一点还需要直线轴另外提供空间位置补偿量才能实现。

模式 3 (TCP,3)

mode permits to use CAD programs in which the tool length, radius, corner radius and contact ahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ngles are different from the ones with which the program (machine coordinates) was generated.该模式 下刀长和半径差异必须通过$TCPWRT 指令输入（参考PLUS Library Manual手册）。

和(TCP,1)一样，为了保持刀尖贴着直线轴所定义的工件轮廓，直线轴会自动根据刀长，半径等自动添加直线轴的补偿量来实现。

[此处图片未下载成功]

Profile obtained without

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

TCP=1 or TCP=3

没有应用TCP 1 或者 TCP 3时的路径 参考程序： G0 X0 A45

X50 A0 F1000 G01 X100 A-45

应用TCP 1 或者 TCP 3时的路径   模式 2 (TCP,2) 模式2是模式1的扩展。

addition to (TCP,1) features, Mode 2 incorporates a move of the horizontal rotary axis so that its inclination remains constant throughout the profile defined by the first two linear axes configured in the TCP table.

horizontal rotary axis move may be generated:

between two elements, to allow for rotation on bevels. In this case, the horizontal rotary axis moves either between thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544he end of an element and the start of the subsequent one, or while the subsequent element is executed (refer to the Threshold Angle parameter).   on a circular element, to keep inclination constant throughout the element. In this case the element and the horizontal rotary axis move will occur simultaneously.

rules apply to all the elements in the profile except for the first one. In fact, the first element is seen as the profile start point even when it is circular and therefore involves no rotary axis move. The system will start generating the horizontal rotary axis move from the second element.

[此处图片未下载成功]

(TCP,4) permits the inclination of the horizontal rotary axis to remain constant throughout the profile defined by the first two linear axes configured in the TCP table.

horizontal rotary axis is adjusted continuously, i.e. between each pair of interpolated points rather than between twhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544o elements as in (TCP,2).

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

For this reason the profile must not be discontinuous. If it is, a &quot;SERVO ERROR&quot; may occur.

[此处图片未下载成功]

(TCP,4) does NOT include the features of (TCP,1).

This mode permits to execute moves in the tool direction.

(TCP,5) is active the system generates a virtual axis whose name has been configured in AMP ( VIRTUAL AXES section of the process configuration).

virtual axis move generates a move of the linear axes in which the tool displaces in its direction, i.e. in the direc(TCP,5) may be programmed both separately or in conjunction with the other axes, in which case (TCP,5) features add to (TCP,1) features. may be moved manually.

5 may be used for drilling inclined holes. Also, it may be used for remohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ving the tool from the part when a failure interrupts the machining cycle. When this oxccurs, we may have three different cases: A) (TCP,5) is enabled, the rotary axes are not homed, and the interruption occurred during a cycle using any TCP mode.

this case the system automatically selects the tool direction according to the position of the rotary axes before the failure. The same may occur after power off, because the rotary axes position is stored in the permanent memory. The values that determine the rotary axes position may be altered via machine logic by means of the MANUAL SETUP data entry or the $TCPWRT function. In particular, $TCPWRT permits to alter the direction in which the tool will be extracted. B) (TCP,5) is enabled, the rotary axes are not homed, and the interruption occurred during a cycle not using TCP.

this case the system must be given the tool direction, i.e. the position of the rotary axes,http://www.wendangwang.com/doc/efe960bed681037ac6d62544 because the stored values may not be significant. The rotary axes position may be input via machine logic by means of the MANUAL SETUP data entry or the $TCPWRT function. C) (TCP,5) is enabled, the rotary axes are homed.

this case the tool direction is given by the current rotary axes position rather than by their position when the interrupt occurred, no matter whether a TCP mode was active during the previous move. However, in normal working conditions stored and current rotary axes positions coincide. NOTE:

more information about the MANUAL SETUP data entry or the $TCPWRT function please refer to the PLUS Library Manual and the User Manual.

用TCP,5把刀移出去 注意：

在所有的TCP模式中，机器PLC会实时把用户表格中的参数386, 399, 400, 358和359发到插补器，因此可以在加工过程中补偿刀具磨损（参考PLUS Library Manual手册中的$TCPWRT）。

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

编程 &quot;m&quot; 和&quot;n&quot; 参数 (角度)

在上http://www.wendangwang.com/doc/efe960bed681037ac6d62544述的TCP模式中，可以编写&quot;m&quot; 和&quot;n&quot;参数，意义如下： m angle subtended between the tool center and the point of contact of the tool with the piece (coincides with U.T. parameter 400) - see figures 2.1, 2.5 and 2.6. n angle of contact between cutting corner and piece (coincides with parameter 359) see figures 2.5 and 2.6.

通过编程这些参数(先通过U.T. 参数 359 设成 1)，你可以使得在下一个程序段改变刀和工件接触点的位置  示例：

[此处图片未下载成功]

X10Y0m270 (TCP,1) G1XY X10Y10

X12Y12|10J12m180 G1X12Y20 (TCP)

编程&quot;m&quot;, &quot;n&quot;, &quot;o&quot; 和“u”, “v”, “w” 参数(向量)

all the TCP utilisation modes described above, in addition to the axis positions it is possible to program the &quot;m&quot;, &quot;n&quot;, &quot;o&quot; which stand for the 3 components of the vector normal to the section to be machined, and the “u”, “v”, “w” parameters denoting the paraxial compensation factors to which the tool radius compensation must http://www.wendangwang.com/doc/efe960bed681037ac6d62544be applied.

programming these parameters it is possible to change the piece-tool contact point from one block to another and through this vector you can obtain the tool diameter compensation.

enable tool radius compensation by means of the “m”, “n”, “o” parameters, set variables T.U. 360 and T.U. 366 on 2. These parameters are applied to the 1st, 2nd, 3rd axis configured in the TCP table.

enable tool radius compensation by means of the “u”, “v”, “w” parameters set the T.U. 360 variable on 0 and the T.U. 366 variable on 3. These parameters are applied to the 1st, 2nd, 3rd axis configured in the process.

用“m”, “n”, “o”编程的例子: m..n..o..  h1

(TCP,....)

;向量初始值 ;TCP activation

用“u”, “v”, “w”编程的例子  h1

(TCP,....) ;激活TCP X..Y..Z.. AB u..v..w.. X..Y..Z.. AB u..v..w.. X..Z..u..v..w.. A..B..u..v..w.. X..Y.. . . . . .

(TCP)

..Y..Z.. AB m..n..o.. X..Y..Z.. AB m..nhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544..o.. X..Z.. m..n..o..  A..B.. m..n..o.. X..Y.. . . . . .

(TCP)

[此处图片未下载成功]

TCP - Tool Center Point for generic 5-axis machines

feature permits programming of a 5-axis machine (with 3 linear   2 rotary axes) irrespective of tool orientation and type (spherical or toroidal). The position controlled by the system is that of the point of attachment of the tool in the spindle (see figures 2.7 and 2.8).

algorithm may be activated simply by programming the TCP code in a block; it is disabled by programming (TCP) or by giving a RESET command. 语法 (TCP[,n])

其中： n Offset mode code (1, 3, 5); the various modes are illustrated in the pages that follow.

说明：

the TCP block you must also write information about the current tools: these tools must be inserted in the &quot;User Table&quot; - abbreviated U.T.

are three tools you can use for entering data ihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544n the user table: the user table editor, the specific machine logic functions, or the L variables in the program.

you may upload the predefined configuration files available with the SETUP utility of the USER TABLE EDITOR. NOTES:

more information about user table management from PLUS refer to the description of $TBLPUTD and $TBLGETD functions in the PLUS Library Manual.

To access the user table from the TABLE EDITOR environment refer to the User Manual.

[此处图片未下载成功]

以下的图片是阐明关于球面刀尖和平头刀尖的参数，U.T.代表用户表格。

[此处图片未下载成功]

(U.T. 358)

图 2.7 平头刀尖

[此处图片未下载成功]

图 2.8 平头刀尖

TCP Table for generic 5-axis machines

[此处图片未下载成功]

Prima Electro S.p.A.

of manual

K

Dynamics

[此处图片未下载成功]

Prima Electro S.p.A.

of manual

Table 365

inhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 PLUS user table Record 92 - Var 1

Progra m L364

P 1 3 5

interpolation mode 1, this parameter defines whether acceleration/deceleration ramps will be used for rotary axes or whether velocities proportional to the linear axes moves will be used. Allowed values are as follows: 0 - No ramps 1 - Ramps If 1 is selected, the velocity diagram will be calculated using the configured parameters for rotary axes, irrespective of linear axes moves. Defines the modalities of activation of the length corrector and the tool radius (and possibly the tool corner radius based on the TTR variable). 0 = values taken from the TCP table 1 = values with sign active in the system (length 1 and tool radius) 2 =absolute values active in the system (length 1 and tool radius) 3 = absolute value of length 1 only; the tool radius is considered = 0. 4 = lengh 1 value with sign; tool radius is =0 http://www.wendangwang.com/doc/efe960bed681037ac6d62544未使用. See end of chapter NOTE: Since part programs are typically referred to the tool tip, program block control is also referred to the to

tip. Real time control is referred to the center of rotation of the axes. When the system detects that the point is beyond the configured limit, it gives an error signal and locks the axes motion with deceleration.

mode

92 - Var 2

2 3 5

move Travel control limits

368

92 - Var 3 Record 92 - Var 4

L367

3 5

K

[此处图片未下载成功]

Programming

this type of TCP, for all the modes described below, both direction (orientation) of the tool and normal direction on the surface to be machined must be defined.

vectors are associated with each point programmed, one normal on the surface being machined (parameters m,n,o) and one reprhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544esenting the tool direction (parameters i,j,k).

parameters m, n, o and i, j and k must be programmed in alphabetical order (e.g. mno, mo, no, ijk,

[此处图片未下载成功]

ik, etc are correct; nmo, on, om, jik, ki, etc. are incorrect).

[i,j,k]

[此处图片未下载成功]

语法

[XYZ] [AB] [m n o]  [i j k]

其中：

of axes

normal vector on surface being machined ijk vector representing tool direction

说明：

the parameters are optional; if none are programmed, the previous programming values are reconfirmed.

activation of TCP, initial position of the two vectors must be defined, by programming values for them (this block does not cause any movement).

TCP active, it is not possible to program m n o and i j k without a movement of the axes XYZAB; furthermore, the vector the define must not be null ([0,0,0]). NOTE:

RESEhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544T command resets the axes.

示例

..n..o..  i..j..k..

;初始向量 ;激活TCP

(TCP,....)    X..Y..Z..  A..B.. m..n..o..  i..j..k. X..Y..Z..  A..B.. m..n..o.. X..Z..  m..n..o..  i..j..k. A..B.. m..n..o.. X..Y..  i..j..k. . . . .

(TCP)

[此处图片未下载成功]

Mode 1 (TCP,1)

(TCP,1) programmed coordinates are referred to the part.

mode must be used when the profile must be executed with both linear (1&#247;3) and rotary (1&#247;2) axes, the tool is expected to remain permanently in contact with the machining surface, and the linear axes coordinates are referred to the part.

keep the tool tip on the profile defined by the linear axes, the system offsets displacements by automatically adjusting the position of the three linear axes to the rotary axes.

Mode 3 (TCP,3)

mode permits to use CAD programs in which the tool length, radius andhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 corner radius are different from the ones with which the program (machine coordinates) was generated.

length, radius and corner radius variances must be input via machine logic (refer to the $TCPWRT instruction in the PLUS Library Manual).

with (TCP,1) in order to keep the tool tip on the profile defined by the linear axes, the system offsets displacements due to variations of length and radii by automatically adjusting the position of the three linear axes to the rotary axes.

[此处图片未下载成功]

Profile obtained without

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

TCP=1 or 3

obtained without TCP1 or 3 active

Prima Electro S.p.A.Type of manual  Mode 5 (TCP,5) This mode permits to execute moves in the tool direction. When (TCP,5) is active the system generates a virtual axis whose name has been configured in AMP ( VIRTUAL AXES section of thehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 process configuration). The virtual axis move generates a move of the linear axes in which the tool displaces in its direction, i.e. in the direction indicated by the vector [i,j,k]. (TCP,5) may be programmed both separately or in conjunction with the other axes, in which case (TCP,5) features add to (TCP,1) features. The move may also be made manually. Mode 5 may be used for drilling inclined holes. NOTE: For more information about the MANUAL SETUP data entry or the $TCPWRT function please refer to the PLUS Library Manual and the User Manual.Removing the tool with TCP,5 NOTE: In all TCP modes, the machine logic may send to the interpolator in real time any variance of tool length, tool radius, or of the corner radius, (parameters 386, 399 and 358 in the User Table). This permits to offset tool wear during machining (refer to the description of the $TCPWRT function in the PLUS Library Manual).45004457K161

Prima http://www.wendangwang.com/doc/efe960bed681037ac6d62544Electro S.p.A.Type of manual  TCP - Tool Center Point for machines with fixed tool and rotary table This performance allow an easy programming on machines in which the tool is in a fixed position and the part moves by means of three axes, two linear ones and a rotary one solid to the linear ones. The system identifies in real time, according to the rotary axis position, the points that the axes must reach to satisfy the programmed profile. It is also possible to make the system calculate the rotary axis position and therefore to define the plane profile defined by the two linear axes. The activation of this algorithm is carried out directly in the program by means of the three-letters TCP. The TCP mode is disabled with (TCP) or with RESET. 语法 (TCP[,n]) 其中： n Type of desired compensation (1, 2,) 说明： The TCP algorithm needs, for its functioning, of some information relative to the used tool, which have to be inserted into the “Ushttp://www.wendangwang.com/doc/efe960bed681037ac6d62544er Table” - abbr..U.T. The “User Table” compilation may be executed by means of the proper editor, or by the machine logic (by means of proper logic functions), or also from part program by means of L variables. It is possible to use a system configuration already pre-arranged contained in the files chargeable by means of &quot;SETUP&quot; of USER TABLE EDITOR. NOTE: For further information relative to the use of the “User Table” read the functions description from PLUS $TBLPUTD and $TBLGETD in the manual of PLUS library. To use the same table from TABLE EDITOR environment see the User manual.45004457K162

Prima Electro S.p.A.Type of manualTCP Table for machines with fixed tool and rotary table Variable User Record in PLUS Part Table User Table Program Offset mode code 385 Record 97 - Var 1 L384MeaningTCPDefines the offset calculation mode according to the machine configuration. NOTE: Must be set with valuhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e = 8. 未使用 Number of the active tool holder 1 &#247;4 未使用. 未使用.1 2Tool length Active tool holder Parameter A Horizontal offset Horizontal rotation head head386 387 388 389 390Record 97 - Var 2 Record 97 - Var 3 Record 97 - Var 4 Record 98 - Var 1 Record 98 - Var 2L385 L386 L387 L388 L3891 2Defines the rotation direction of 1 the rotary axis (table) and has a 2 value of:   1 clock-wise - 1 anticlock-wise for positive programming 未使用. ID of the axis to be used as abscissa in the offset algorithm. ID of the axis to be used as ordinate in the offset algorithm. 未使用. ID of the rotary axis (table) 未使用 未使用. 未使用. 未使用. It defines the angle between the tool center and the cutter contact point after having rotated the vertical head in order to have the tool orientated in y-direction 1 2 1 2 1 2 1 2 1 2Vertical rotationhead391 392 393 394 395 396 397 398 399 400Record 98 - Var 3 Record 98 - Var 4 Record 99 - Var 1 Record 9http://www.wendangwang.com/doc/efe960bed681037ac6d625449 - Var 2 Record 99 - Var 3 Record 99 - Var 4 Record 100 Var 1 Record 100 Var 2 Record 100 Var 3 Record 100 Var 4L390 L391 L392 L393 L394 L395 L396 L397 L398 L3991st linear axis ID 2nd linear axis ID 3rd linear axis ID Horizontal ID headVertical head ID Horizontal inclination Vertical inclination Radius Angle head head45004457K163

Prima Electro S.p.A.Type of manualTool holder 1 VariableUser Table 369Record in PLUS user table Record 93 - Var 1 Record 93 - Var 2 Record 93 - Var 3 Record 93 - Var 4Part Progra m L368MeaningTC P 1 2 1 2Parameter BSign distance expressed in mm of the table centre from the tool tip as regards the abscissa axis. Sign distance expressed in mm of the table centre from the tool tip as regards the ordinate axis. 未使用 未使用Parameter C370L369Parameter D Offset head vertical371 372L370 L371Tool holder 2 VariableUser Table 373Record in PLUS user table Record http://www.wendangwang.com/doc/efe960bed681037ac6d6254494 - Var 1Part Progra m L372MeaningTCPParameter B (figures 2.1, 2.3) Parameter C (figures 2.1, 2.2) Parameter D Vertical offset Tool holder 3 Variable headAs in tool holder 11 2 1 2374Record 94 - Var 2L373As in tool holder 1375 376Record 94 - Var 3 Record 94 - Var 4L374 L375未使用 未使用User Table 377 378 379 380Record in PLUS user table Record 95 - Var 1 Record 95 - Var 2 Record 95 - Var 3 Record 95 - Var 4Part Progra m. L376 L377 L378 L379MeaningTC P 1 2 1 2Parameter B Parameter C Parameter D Offset head verticalAs in tool holder 1 As in tool holder 1 未使用 未使用Tool holder 4 VariableUser Table 381Record in PLUS user table Record 96 - Var 1Part Progra m L380MeaningTC P 1 2Parameter BAs in tool holder 145004457K164

Prima Electro S.p.A.Type of manualParameter C Parameter D Offset head vertical382 383 384Record 96 - Var 2 Record 96 - Var 3 Record 96 - Var 4L3http://www.wendangwang.com/doc/efe960bed681037ac6d6254481 L382 L383As in tool holder 1 未使用 未使用1 2Dynamics Variable Dynamic modeUser Table 357Record in PLUS user table Record 90 - Var 1Part Program L356Meaning These fields may have the following values: 0 - Speeds and accelerations of linear axes are not limited, and may exceed the configured values run time 1 - Speeds of linear and rotary axes are limited run time, if necessary, in such as never to exceed the configured values. Accelerations of the linear and rotary axes are limited in advance so that overlapping of movements does not require accelerations in excess of those configured. 2 - Speeds and accelerations of the linear and rotary axes are limited in advance so that the speeds and accelerations calculated run time never exceed the configured values. In this case, if for example only the linear axis is moved, it remains limited unlike what happened in case 1. It must be stressed that in case 2, the constant speed http://www.wendangwang.com/doc/efe960bed681037ac6d62544is guaranteed on the profile, which does not happen in case 1 if speed of an axis is cut run time. 未使用 未使用 未使用TC P 1 2Corner radius&#185; Angle of contact a Programming of &quot;m&quot;, &quot;n&quot; and &quot;o&quot;358 359 360Record 90 - Var 2 Record 90 - Var 3 Record 90 - Var 4L357 L358 L35945004457K165

Prima Electro S.p.A.Type of manualThreshold angle (figure 2.4)361Record 91 - Var 1L360Angle beyond which the system adds a horizontal rotary axis move --after the element has been completed-- in order to position the tool perpendicular to the subsequent element. Below this angle, the horizontal rotary axis move starts when the element is completed and continues during execution of the subsequent element. Velocity expressed in degrees per minute at which the horizontal rotary axis moves when it is automatically positioned between two part program blocks. If it is 0 the system uses the prograhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544mmed feedrate.2Rotary velocityaxis 362Record 91 - Var 2L3612Dynamics (continued) Variable User Table Interpolation mode 363Record in PLUS user table Record 91 - Var 3Part Progra m L362MeaningTC P 1 2Specifies whether or not the rotary axes are interpolated in conjunction with the linear axes. If not interpolated, the rotary axes follow the linear axes moves. Allowed values are: 0 - Rotary axes interpolated in conjunction with linear axes 1 - Rotary axes follow linear axes Select mode 1 if the velocity on the profile should not be affected by rotary axes motion. Specifies whether the rotary axes must be interpolated only by the error or must be treated as linear axes. Allowed values are: 0 - Rotary axes interpolated as linear axes 1 - Rotary axes interpolated only by the error.Interpolation type364Record 91 - Var 4L3631 245004457K166

Prima Electro S.p.A.Type of manualIntegratorhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544365Record 92 - Var 1L364With interpolation mode 1, this parameter defines whether acceleration/deceleration ramps will be used for rotary axes or whether velocities proportional to the linear axes moves will be used. Allowed values are as follows: 0 - No ramps 1 - Ramps If 1 is selected, the velocity diagram will be calculated using the configured parameters for rotary axes, irrespective of linear axes moves. 未使用 Specifies the minimum angle beyond which the system automatically generates a move of the horizontal rotary axis in order to position the tool perpendicular to the subsequent element.1 2Offset mode Minimum move366 367Record 92 - Var 2 Record 92 - Var 3L365 L366245004457K167

Prima Electro S.p.A.Type of manualDynamics (continued) Variable User Table limits 368 Record in PLUS user table Record 92 - Var 4 Part Progra m L367 Meaning TC P 1 2Travel controlDefines how the configured trahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544vel limits will be controlled. Allowed values are: 0 - travel limits controlled both in the program block (before execution) and at each point in real time. 1 - travel limits controlled both only at each point in real time. NOTE: Since part programs are typically referred to the tool tip, program block control is also referred to the tool tip. Real time control is referred to the center of rotation of the axes. When the system detects that the point is beyond the configured limit, it gives an error signal and locks the axes motion with deceleration.NOTE: In the above tables distances are expressed in mm. They must be intended in the configured length unit.45004457K168

Prima Electro S.p.A.Type of manual3.67.1ProgrammingThe rotary table virtualization allows the programming of machines with tool in fixed position and the part moving by means of three axes, two linear ones and one rotary solid to the two linhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ear ones. It is activated by commands (TCP, 1) or (TCP, 2). By programming (TCP, 2) the automatic insertion of rotary axis is obtained. (TCP, 1) and (TCP, 2) performances and characteristics described for 5-axis machines are valid also for this kind of compensation. For a correct programming on rotary table machines, the following must be taken into consideration: a) the system considers to have, at the end of the homing cycle, coincident tool tip and table centre. In case this situation does not happen, the values representing the distance of the tool centre from the tool tip must be defined in the TCP table (T.U.369 e T.U. 370) b) the profile must be defined as regards an origin coincident with the table centre, therefore, as described in the previous point, if table centre and tool tip do not coincide, the origin must be defined with the two values of abscissa and ordinate equal to the phase displacement defined in the TCT tablehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 (T.U. 369 e T.U. 370). Example:A = 10 mmTABLE IN POSITION 0T.U. 369AT.U. 370TOOL IN POSITION 0XT.U. 369 = - 40 T.U. 370 =   110 ORIGIN 1 (POINT O) X-40 (UOT,1,X-70,Y-70) GX-10Y-10 (TCP,2) G1 Y0 F2000 X 140 Y 130 G3 X0 Y130 I70 J90 G1Y-10 (TCP)Distance, as regards X, of the table centre from the tool tip Distance, as regards Y, of the table centre from the tool tip Y 110 ; POINT A45004457K169

Prima Electro S.p.A.Type of manual 3.68TCP - Tool Center Point for machines with Prismatic HeadThis function is used to program a machine with 5 axes (3 linear and 2 rotary axes) with reference to the tip of the tool rather than the rotation centre of the axes (centre of the head). It differs from the standard Double Twist Head, in that the vertical rotary axis rotates in a plane not orthogonal to the plane of the horizontal rotary axis. The activation of this algorithm is performed directly in the phttp://www.wendangwang.com/doc/efe960bed681037ac6d62544rogram through the TCP triliteral. The TCP mode is disabled with (TCP) or RESET. It is possible to program this type of head by regarding it as a standard Double Twist Head (rotation of an axis in the horizontal plane and the other axis in a vertical plane), in this case, the system sees to the adjustments needed. The TCP mode is disabled with (TCP) or RESET. 语法 (TCP[,n])其中： n Type of compensation desired (1 5); these modes are described in the previous pages.说明： To work, the algorithm of TCP requires some data on the tool being used. The head managed accepts a single vertical or angular tool. The configuration parameters must be evaluated after positioning the head so that the tool is arranged vertically along the Z- direction and the rotation axis of B is parallel to the XZ plane as shown in figures 2.9, 2.10, 2.11. These parameters must be entered in the &quot;User Table&quot;. The User Table can be compiled by means of the http://www.wendangwang.com/doc/efe960bed681037ac6d62544ad hoc editor or through the machine logic (through the ad hoc logic functions), or by means of the part program through the L variables. It is possible to use a configuration already predisposed by the system, which is contained in files that can be loaded through the &quot;SETUP&quot; of the USER TABLE EDITOR. These files are called TCP7_ITA and TCP7_ENG. NOTES: For further information on the use of the User Table from PLUS, read the description of the $TBLPUTD and $TBLGETD functions in the manual of the PLUS library. For the use of the same table in the TABLE EDITOR environment, see the User Manual.45004457K170

Prima Electro S.p.A.Type of manualTCP table for machines with &quot;Prismatic&quot; head Variable User PLUS user table Part table records Progra m Type of compensation 385 Record 97 - Var 1 L384Meaning of the variableTC P 1 2 3 5Defines the compensation calculation mode as a function of machine http://www.wendangwang.com/doc/efe960bed681037ac6d62544configuration. NOTE: set a value of 7 Defines the length of the tool currently fitted to the machine.Tool length  386Record 97 - Var 2 Record 97 - Var 3 Record 97 - Var 4L3851 2 5Free Horizontal head offset  387 388L386 L387 It is the offset value, expressed in degrees, to be associated with the axis of the horizontal head in order to have the plane containing the tool coincide with the XZ plane of the machine. To determine this offset rotate the horizontal axis so that the plane containing the tool coincides with the XZ plane and that, after this rotation, a positive movement of the tilting head aims the tool towards Z-. At this point, take the value displayed on the screen, multiply it by the direction of rotation of the horizontal head and change the sign. It is the offset value, expressed in degrees, to be associated with the axis of the tilting head in order to position the tool along the Zdirection. To determihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ne this offset rotate the tilting axis to move it in the position previously specified. At this point, take the value displayed on the screen, multiply it by the direction of rotation of the tilting head and change the sign. 1 2 3 4 5Tilting offset  head389Record 98 - Var 1L3881 2 3 4 545004457K171

Prima Electro S.p.A.Type of manualDirection of horizontal head   (figure 2.11)390Record 98 - Var 2L389Defines the direction of rotation of the horizontal head viewed from the top, and it is:  1 for the clockwise direction - 1 for the counter clockwise direction in positive programming. Defines the direction of rotation of the tilting head viewed from the left side and it is:  1 for the clockwise direction - 1 for the counter clockwise direction in positive programming.1 2 3 4 5 1 2 3 4 5Direction of tilting head   (figure 2.10)391Record 98 - Var 3L390From this point on, it continues ashttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 standard” Double Twist” table.45004457K172

Prima Electro S.p.A.Type of manualHead Table Variable User table 369 PLUS user table records Record 93 - Var 1 Part Progra m L368 Meaning TC P 1 2 5Parameter A  Distance along the first axis (X) between the control point Pc and the rotation point Pr. This distance must be expressed in mm and has a positive value when the transition from Pc to Pr takes place along the negative direction of the axis. Distance along the second axis (Y) between the control point Pc and the rotation point Pr. This distance must be expressed in mm and has a positive value when the transition from Pc to Pr takes place along the negative direction of the axis. Distance along the third axis (Z) between the control point Pc and the rotation point Pr. This distance must be expressed in mm and has a positive value when the transition from Pc to Pr takes place along the negative direction of thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544he axis. Distance along the first axis (X) between the rotation point Pr and the tool attachment point Pu. This distance must be expressed in mm and has a positive value when the transition from Pr to Pu takes place along the negative direction of the axis. Distance along the second axis (Y) between the rotation point Pr and the tool attachment point Pu. This distance must be expressed in mm and has a positive value when the transition from Pr to Pu takes place along the negative direction of the axis. Distance along the third axis (Z) between the rotation point Pr and the tool attachment point Pu. This distance must be expressed in mm and has a positive value when the transition from Pr to Pu takes place along the negative direction of the axis.Parameter B   (figures 2.10 and 2.11)370Record 93 - Var 2L3691 2 5Parameter C   (figures 2.9 and 2.11)371Record 93 - Var 3L3701 2 5Parameter D   (figures 2.9 and 2.11)http://www.wendangwang.com/doc/efe960bed681037ac6d62544372Record 93 - Var 4L3711 2 5Parameter E  373Record 94 - Var 1L3721 2 5Parameter F   (figures 2.9 and 2.11)374Record 94 - Var 2L3731 2 545004457K173

Prima Electro S.p.A.Type of manualInclination (figure 2.9)375Record 94 - Var 3L374Inclination of the axis around which the tilting axis rotates relative to the machine vertical. Defines the programming mode of the tilting axis and is: With 0 it is programmed in terms of transducer dimensions (degrees relative to its axis of rotation). With 1 it is programmed in terms of transducer dimensions (as in 0), but the horizontal rotary axis is automatically oriented by the system so that, no matter how the tilting axis is moved, the tool remains in the plane defined by the dimensions programmed on the horizontal rotary axis. With 2 the inclination of the tilting axis is not programmed with reference to the transducer but rather in terms http://www.wendangwang.com/doc/efe960bed681037ac6d62544of inclination in space; 0 is defined with the tool aimed towards Z-; at all events, the horizontal rotary axis is oriented automatically. In the latter case, the programming of the head is the same as the programming of a standard double twist head. It is used solely for programming mode 2. It is the positive limit programmable. Its maximum value is determined on the basis of the value given in the &quot;inclination&quot; field as: acos(2*sin2(90-incl)-1). It is important to set the lower limit of this value, as around it the speed of the tilting axis approaches   and thereby generates a servo error.1 2 3 5 1 2 3 5Tilting axis management mode376Record 94 - Var 4L375  operational limit of tilting axis377Record 95 - Var 1L3761 2 3 545004457K174

Prima Electro S.p.A.Type of manualoperational limit of tilting axis378Record 95 - Var 2L377It is used solely for programming mode 2. It is thehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 negative limit programmable. Its minimum value is determined on the basis of the value given in the &quot;inclination&quot; field as: -acos(2*sin2(90-incl)-1). It is important to set the upper limit of this value, as around it the speed of the tilting axis approaches   and thereby generates a servo error.1 2 3 5Offset of tilting axis  379Record 95 - Var 3L378It is used solely for programming mode 2. It is the offset value, expressed in degrees, to be associated with the tilting axis in order to position the tool along the Z- direction. To determine this offset rotate the tilting axis so that the tool is moved to the position specified earlier. At this point, take the value displayed, multiply it by the direction of the tilting axis and change the sign. It is used solely for programming mode 2. It defines the direction of rotation of the tilting axis viewed from the left side and is:  1 for the clockwise direction - 1 fhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544or the counter clockwise direction in positive programming1 2 3 5Direction of tilting axis  380Record 95 - Var 4L3901 2 3 4 53.69ANGULAR TRANSMISSIONA PRISMATIC head with angular transmission (figure 2.12) must be characterised by considering initially the tool in a vertical position and by determining the parameters of the head movements accordingly. After that, with the B rotation axis parallel to the XZ plane and starting from the position of the tool along the Z- direction, arrange the angular transmission in the appropriate working position and determine the other four tool parameters. An angular head, in fact, is always identified by four parameters, i.e., two lengths and two angular measurements. The two lengths (offset in the direction of the Z axis) reflect the following distances: from the centre of the head to the centre of the angular transmission (L2) and from the centre of the transmission to the cenhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544tre of the relative spindle (L1). The two angular measurements correspond to the upward and transverse movements of the tool holder: offset around X (beta) and offset around Z (alpha)45004457K175

Prima Electro S.p.A.Type of manual3.69.1VariableAngular transmission tableUser table 381 PLUS user table records Record 96 - Var 1 Record 96 - Var 2 Record 96 - Var 3 Part Progra m L380 Meaning TC P 1 2 5 1 2 5 1 2 5 1 2 5Length 1   (figure 2.12) Length 2   (figure 2.12) Angle alpha   (figure 2.12)Defines length L1 in mm382L381Defines length L2 in mm383L382Defines the phase displacement angle  , in degrees, of the transmission around the Z axis. (-180&#176;       180&#176;).Angle beta   (figure 2.12)384Record 96 - Var 4L383Defines the inclination  , in degrees, of the transmission relative to the Z- axis. (-90&#176;       90&#176;).   This parameter can be varied continuously through lowhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ercase (tcp,n) programming. For the compilation of the Dynamic table see the table for the standard “Double Twist” machine. The figures below illustrate the compensation characterisation parameters applied to a machine shown in schematic front, side and top views. Z  D PcAxis of rotation of horizontal headControl point CInclin. Axis of rotation of tilting headPr  F Pu Pw -X -Z图 2.9 Front view X45004457K176

Prima Electro S.p.A.Type of manual ZAxis of rotation of horizontal head BControl pointPcAxis of rotation of tilting head C Pr  FclockwisePu Pwcounterclockwise Direct. of rotation of tilting head Y -Z图 2.10 Side view-Y  Y  D Pc  B Puclockwise Axis of rotation of tilting head Control point Axis of rotation of horizontal headPrcounterclockwise-X Y图 2.11 Top view X45004457K177

Prima Electro S.p.A.Type of manualAn angular tool, as shown in the figurhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e, is characterised by four parameters: length L1, length L2, phase displacement angle   around axis Z, inclination   of the tool relative to axis Z-.ANGULAR TOOLZAngleY Y18 0&#176;  18 0&#176;   P u L 1X X0 &#176; Angle Angle  L 2Tool directioncounter  clockwis eZ P w   Tool direction 9 0&#176;9 0&#176;YAnglecloc    kwiseTool direction0 &#176;图 2.123.69.2ProgrammingWith the same functional specifications it is possible to use all the TCPs admissible for the double twist head. It is also possible to program both using the m,n,o versors normal to the piece and the contact angles, m and n.45004457K178

Prima Electro S.p.A.Type of manual 3.70TCP - Tool Center Point for machines with rotary axis plus balancing axis (Mixed)This function is used to program a 5-axes machine (3 linear and 2 rotary) with reference to the tool head rather than the rotation centre of thehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 axes (centre of the head). It differs from the standard Double Twist Head as the machine has a “mixed” kinematics with a rotary axis on a bench and a balancing axis. Rotary axis (or rotary table) rotates on a plane parallel to the machine vertical axis, it means its rotary axis is placed on the XY plane (if the tern is XYZ axes) rotated towards to the X direction: the part is fastened on it. On the contrary, balancing rotary axis, rotates within one of the three main manchine planes; its rotary axis must coincide with one of the three TCP axes, placing the tool on the part.The TCP mode is disabled with (TCP) or RESET. 语法 (TCP[,n])其中： n Type of compensation desired (1, 3, 5); these modes are described in the previous pages. 说明： The algorithm of TCP requires some data about the tool in use to became operative. On the rotary balancing axis can be fixed up to two heads. The configuration parameters must be evaluated after positioninhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544g the axes in 0. These parameters must be entered in the &quot;User Table&quot;. The User Table can be compiled by means of the ad hoc editor or through the machine logic (through the ad hoc logic functions), or by means of the part program through the L variables. It is possible to use a configuration already predisposed by the system, which is contained in files that can be loaded through the &quot;SETUP&quot; of the USER TABLE EDITOR. These files are called TCPM_ITA and TCPM_ENG. This type of compensation can be used with the three-letter codes (UPR, 0 and (UPR, 2; all the other UPR modes are not available. NOTE: For more info about “user table” use from PLUS, please read the $TBLPUTD and $TBLGETD funcrions description on the library PLUS manual. To use the same table from TABLE EDITOR refer to the User Manual3.70.1VariableTPC table for machines with “Mixed” headUser table 385 PLUS user table records Record 97 - Var 1 Parthttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 Progra m L384 Meaning of the variable TC P 1 2 3 5Type of compensationDefines the compensation calculation mode as a function of machine configuration. NOTE: set a value of 945004457K179

Prima Electro S.p.A.Type of manualTool length  386Record 97 - Var 2 Record 97 - Var 3 Record 97 - Var 4L385Defines the length of the tool currently fitted to the machine. Active tool holder number 1 2.1 2 5 1 3 5 1 3 5 1 3 5Active holder *tool387L386Direction balancing axis *388L387TCP axis index around which the balancing axis rotates. It is 1 for the first TCP axis, 2 fro the second and 3 for the third. It is an angle value defining the angle around which rotary axis rotates between therotary axis and the positive direction of the first axis of the TCP configuration. Defines the direction of rotation of the horizontal head viewed from the right side, and it is: -1 for the clockwise direction  1 http://www.wendangwang.com/doc/efe960bed681037ac6d62544for the counter clockwise direction in positive programming. Defines the direction of rotation of the balancing head viewed from the top and it is: -1 for the clockwise direction  1 for the counter clockwise direction in positive programming.Rotary axis orientation *389Record 98 - Var 1L388Direction rotary axis   (figure 2.14)of390Record 98 - Var 2L3891 3 5Direction of balancing axis*  (figure 2.13)391Record 98 - Var 3L3901 3 5From this point on, it continues as standard” Double Twist” table.3.70.2Variable Parameter D1*Rotary axes tableUser table 369 PLUS user table records Record 93 - Var 1 Part Program L368 Meaning Position along the first TCP axis (X) of the axis around which the roatry axis rotates (Table center). Position along the second TCP axis (Y) of the axis around which the roatry axis rotates (Table center). Position along the third axis (Z) of the axis around which the roatry axis http://www.wendangwang.com/doc/efe960bed681037ac6d62544rotates (Table center). TCP 1 3 5 1 3 5 1 3 5Parameter D2 * (figures 2.13 and 2.14) Parameter D3 * (figures 2.14)370Record 93 - Var 2L369371Record 93 - Var 3L37045004457K180

Prima Electro S.p.A.Type of manualOperating Radius *372Record 93 - Var 4L371Maximum working radius around the rotative table centre. It is used only for dynamic limitatins on the rotary axis. TCP index along which is oriented the first tool; orientation is from the tool head to the spindle. It is 1 for the first TCP axis, 2 for the second and 3 for the third. if the tool orientation direction is different form the axis direction, it has the symbol Distance along the first TCP axis (X) between the first tool spindle and the axis around which the balancing axis rotates. Distance along the second TCP axis (Y) between the first tool spindle and the axis around which the balancing axis rotates. Distance along the third TCP http://www.wendangwang.com/doc/efe960bed681037ac6d62544axis (Z) between the first tool spindle and the axis around which the balancing axis rotates. TCP index along which is oriented the second tool; orientation is from the tool head to the spindle. It is 1 for the first TCP axis, 2 for the second and 3 for the third. if the tool orientation direction is different form the axis direction, it has the symbol Distance along the first TCP axis (X) between the second tool spindle and the axis around which the balancing axis rotates. Distance along the second TCP axis (Y) between the second tool spindle and the axis around which the balancing axis rotates.1 3 5Tool direction axis 1*373Record 94 - Var 1L3721 3 5Parameter B1(1)* (figure 2.13)374Record 94 - Var 2L3731 3 5Parameter B2(1)* (figures 2.13 and 2.14)375Record 94 - Var 3L3741 3 5Parameter B3 (1)* (figure2.14)376Record 94 - Var 4L3751 3 5Tool Direction Axis 2* (figures 2.13 and 2.14)377Rehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544cord 95 - Var 1L3761 3 5Parameter B1 (2) * (figure 2.13)378Record 95 - Var 2L3771 3 5Parameter B2 (2)* (figures 2.13 and 2.14)379Record 95 - Var 3L3781 3 545004457K181

Prima Electro S.p.A.Type of manualParameter B3 (2)* (figure 2.14)380Record 95 - Var 4L390Distance along the third TCP axis (Z) between the second tool spindle and the axis around which the balancing axis rotates.1 3 5Rotary Axis Offset381Record 96 - Var 1L380Offset, measured in degrees, 1 to be applied on the rotary 3 axis in order to match the 5 solid Cartesian tern with the machine Cartesian tern. Offset, measured in degrees, to be applied on the balancing axis as to place tool 1 along the direction described in the “Tool Direction Axis 1”. Offset, measured in degrees, to be applied on the balancing axis as to place tool 1 along the direction described in the “Tool Direction Axis 2”. 1 3 5Balancing http://www.wendangwang.com/doc/efe960bed681037ac6d62544axis offset for tool 1 *382Record 96 - Var 2L381Balancing axis offset for tool 1 *383Record 96 - Var 3L3821 3 5 Changing parameter using minuscule programming (tcp,n).To fill the Dynamic table, please refer to the “Double Twist” standard machine table.图 2.13 From the top45004457K182

Prima Electro S.p.A.CW -1Type of manualY CCW  1 Balancing Rotation CentreZ  Tool DirectionB 2B 2 B 3 Tool DirectionTool Base Rotary Table Rotation Centre Rotary Table D 1 CW -1 D 2 D 2 CCW  1 Zero Machine D 3 Rotation Centre Tool BaseBalancing Rotation Centre B 1X   Y  Zero Machine图 2.14 From the right side3.71TCP - Tool Center Point for machines with double rotary axis on the table (MachineBed)This function is used to program a 5-axes machine (3 linear and 2 rotary) with reference to the tool head rather than the rotation centre of the axes (centre of the head). It differs from thehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 standard Double Twist Head as the machine has a “bench” kinematics with two solid tables (roatary axes) with machine bench: the part is fastened on them; the tool above the part doesn’t rotate. The “second rotary axis” is the one connected to the machine while the “first rotary axis” rotates within the bench supporting the previous rotary axis; the part is fastened above the first rotary axis. Both tables have the rotary axis parallel to one of the machine axes on which is activated the TCP. the tool MUST be build on the third TCP linear axis. The TCP mode is disabled with (TCP) or RESET. 语法 (TCP[,n])其中： n Type of compensation desired (1, 3, 5); these modes are described in the previous pages. 说明： To work, the algorithm of TCP requires some data on the tool being used. The configuration parameters must be evaluated after positioning the axes in 0.45004457K183

Prima Electro S.p.A.Type of manualThese parameterhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544s must be entered in the &quot;User Table&quot;. The User Table can be compiled by means of the ad hoc editor or through the machine logic (through the ad hoc logic functions), or by means of the part program through the L variables. It is possible to use a configuration already predisposed by the system, which is contained in files that can be loaded through the &quot;SETUP&quot; of the USER TABLE EDITOR. These files are called TCPM_ITA and TCPM_ENG. This type of compensation can be used with the triliteral (UPR, 0 and (UPR, 2; all the other UPR modesare not available. NOTE: For more info about “user table” use from PLUS, please read the $TBLPUTD and $TBLGETD funcrions description on the library PLUS manual. To use the same table from TABLE EDITOR read the “User Manual”.3.71.1Variable Type compensationTCP table for machines with head “MachineBedUser table of 385 PLUS user table records Record Var 1 97 Part Program Meaning ofhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 the variable Defines the compensation calculation mode as a function of machine configuration. NOTE: set a value of 10 Defines the length of the tool currently fitted to the machine. TCP 1 3 5- L384Tool length  386Record Var 2 Record Var 3 Record Var 497- L3851 3 5Free Kinematic Rotation (Figure 2.18)387 388 1*97 97- L386 - L387 Value identifying the TCP 1 rotation in order to place the 3&#176; 3 TCP axis along the positive 5 direction of rotary axis of the 1&#176; rotative. If the rotation is around the 1&#176; TCP axis, the value is 1, if the rotation is around the 2&#176;axis the value is 2, if there is no rotation value is 0. If there is an inversion of the 3&#176; TCP axis, the values are 11 and 12 (11 with a rotation in respect to the 1&#176; axis and 12 with a rotation I nrespect of the 2&#176; axis). These values can be set, with reference to the figure 2.18.45004457K184

Prima Electrohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 S.p.A.Type of manualKinematic Rotation (Figure 2.18)389 2*Record Var 198- L388Value identifying the TCP rotation after the previous rotation in order to place the 3&#176; TCP axis along the positive direction of rotary axis of the 2&#176; rotative. If the rotation is around the 1&#176; TCP axis, the value is 1, if the rotation is around the 2&#176;axis the value is 2, if there is no rotation value is 0. If there is an inversion of the 3&#176; TCP axis, the values are 11 and 12 (11 with a rotation in respect to the 1&#176; axis and 12 with a rotation in respect of the 2&#176; axis). These values can be set, with reference to the figure 2.18.1 3 5Kinematic Rotation (Figure 2.18)390 3*Record Var 298- L389Value identifying the TCP 1 rotation after the previous 3 rotation in order to place the 3&#176; 5 TCP axis along the original direction, i.e. the rotation active before all the other rotations. . If the rhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544otation is around the 1&#176; TCP axis, the value is 1, if the rotation is around the 2&#176;axis the value is 2, if the rotation is around the 3&#176; axis the value is 3, if there is no rotation value is 0. If there is an inversion of the 3&#176; TCP axis, the values are 11 and 12 (11 with a rotation in respect to the 1&#176; axis and 12 with a rotation in respect of the 2&#176; axis). These values can be set, with reference to the figure 2.18. Index identifying the type of rotation to be ferformed arounf the TCP vertical axis in order to justify the first two axes of the original tern after the previous rotations. This index is 0, 1, 2 or 3 namely 0&#176;, 90&#176;, 180&#176; or 270&#176;. 1 3 5Kinematic Rotation 4* (Figure 2.18)391Record Var 398- L390From this point on, it continues as standard” Double Twist” table.45004457K185

Prima Electro S.p.A.Type of manual3.71.2Variable Parameter D1*Rothttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ary axes tableUser table 369 PLUS user table records Record 93 - Var 1 Part Program L368 Meaning Position along the first TCP axis (X) of the axis around which the rotary axis rotates (First rotary axis table centre) Position along the second TCP axis (Y) of the axis arounf which the rotary axis rotates (First rotary axis table centre) Position along the third TCP axis (Z) of the axis arounf which the rotary axis rotates (First rotary axis table centre) Maximum manchine radius around the rotation centre of the first table. It is used only for dynamic limitations on the rotary axis. Position along the first TCP axis (X) of the axis around which the secondary rotary axis rotates (First rotary axis table centre) Position along the second TCP axis (Y) of the axis around which the secondary rotary axis rotates (First rotary axis table centre) Position along the third TCP axis (Z) of the axis around which the secondary rotary axis rotathttp://www.wendangwang.com/doc/efe960bed681037ac6d62544es (First rotary axis table centre) Maximum working radius around the second table rotation centre. It is used only for dynamic limitations on rotary axis. TCP 1 3 5 1 3 5 1 3 5 1 3 5Parameter D2* (Figure 2.17) Parameter D3* (Figure 2.17) Operating Radius 1*370Record 93 - Var 2L369371Record 93 - Var 3L370372Record 93 - Var 4L371Parameter B1* (Figure 2.16)373Record 94 - Var 1L3721 3 5 1 3 5Parameter B2*374Record 94 - Var 2L373Parameter B3* (Figure 2.16)375Record 94 - Var 3L3741 3 5 1 3 5Operating Radius 2*376Record 94 - Var 4L375Offset Rotary Axis 1*377Record 95 - Var 1L376Offset in degreesto be associated 1 with the first rotary axis in orde 3 to justify it to the Cartesian tern 5 of the part. Offset in degreesto be associated with the second rotary axis in orde to justify it to the Cartesian tern of the part. 1 3 5Offset Rotary Axis 2*378Record 95 - Var 2L37http://www.wendangwang.com/doc/efe960bed681037ac6d625447Changing parameter using minuscule programmino (tcp,n). To fill the Dynamic table, please refer to the “Double Twist” standard machine table. 45004457K186

Prima Electro S.p.A.Type of manualY B 1 Secondary Rotary table Rotary AxisMain Rotary Table Rotary Axis D 2图 2.15 View from the topZero MachineX  Z Secondary Rotary Table Rotation Centre CW -1B 3CCW  1 B 1Zero MachineX  图 2.16 Front viewZ Main Rotary Table Rotation CentreCW -1D3D2CCWZero machine图 2.17 Side viewY  45004457K187

Prima Electro S.p.A.Type of manualZ -3 -2  3 -1  1 X  1 -3  3 Z  2  2 Y -2 Y-1 Z  1 2 12 11  1 1 X Y X图 2.18 Rotations45004457K188

Prima Electro S.p.A.Type of manual3.71.3TCP on multi-processorThe TCP feature is now extended to 4 processes, each process will use a setup area of its own in the User tables as shown in the table below. Process 1 Tabbhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544le TCP Table Tool-holder 1 Tool-holder 2 Tool-holder 3 Tool-holder 4 Dynamics 2 TCP Table Tool-holder 1 Tool-holder 2 Tool-holder 3 Tool-holder 4 Dynamics 3 TCP Table Tool-holder 1 Tool-holder 2 Tool-holder 3 Tool-holder 4 Dynamics 4 TCP Table Tool-holder 1 Tool-holder 2 Tool-holder 3 Tool-holder 4 Dynamics Plus Table Record Record 97 Record 93 Record 94 Record 95 Record 96 Record 90 Record 86 Record 82 Record 83 Record 84 Record 85 Record 79 Record 75 Record 71 Record 72 Record 73 Record 74 Record 68 Record 64 Record 60 Record 61 Record 62 Record 63 Record 57 Part Program LVariable L384   L368   L372   L376   L380   L356   L340   L324   L328   L332   L336   L312   L296   L280   L284   L288   L292   L268   L252   L236   L240   L244   L248   L224   L399 L371 L375 L379 L383 L367 L355 L327 L331 L335 L339 L323 L311 L283 L287 L291 L295 L279 L267 L239 L243 L247 L251 L2353.71.4REMARKS ON TCP PARAMETERS Dynamic Mode – L356This field http://www.wendangwang.com/doc/efe960bed681037ac6d62544can have the following values: 0. Speed rate, accelerations, jerks and minimum ramp times of the linear axes do not change therefore, when they are moved at the same time of the rotary axes, they can exceed the set values at a run time. Speeds, accelerations, jerks and earliest ramp times of the rotary axes are limited in order to not exceed the dynamic limits of the linear axes. 1. Speed rates of linear and rotary axes do not change; Speed rates, accelerations, jerks and minimum ramp times are limited so that the overlapping axes motions do not require dynamic permormances exceeding those configured for the axes. To avoid the exceeding of the maximum axes velocities, a dynamic limitation algorithm is activated at run time during the overlapping movement of linear and rotary axes. When an axis is about to exceed its acceleration for rapid movement limit, the control reduces the machine feed rate. As the system uses this algorithm lhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ater and can’t exceed the axes acceleration limits, during the regularization the axis acceleration for rapid movement could be exceeded. It can be suggested to program the acceleration for rapid movement lower than the45004457K189

Prima Electro S.p.A.Type of manualmaximum allowed by the axis. 2. Speed rates, accelerations, jerks and minimum ramp times of linear and rotary axes are previously limited as to avoid the axes dynamic limits exceeding. If the linear axis moves, it has anyway a limited speed, as do not happen in the two previous cases. 4. It’s similar to case 0, but rotary axes feed limitation is dynamically recalculated during the movimentation as to match the TCP throat depths. It aims is to not exceed the dynamic limits of the linear axes. 5. It’s similar to case 1. The rotary axes velocity limitation is dynamically recalculated during the movimnetation in order to match the TCP throath depths. It http://www.wendangwang.com/doc/efe960bed681037ac6d62544aims is to not exceed the dynamic limits of the linear axes.3.71.5Operational Limits Mode – L367This field has to be set by bit and can have the following values: bit 0 refers to the management of the TCP linear axes operational limits. If it is 0, during the part program, the system controls if the programmed points exceed the operational limits; with TCP active, programmed points refer to the tool head. In this case, the movement outside the operational limits is not activated displaying an error message. If it is 1, the control is disabled. When TCP is active, the system controls that the motions does not exceed the operational limits when axes are moving; the system controls the points of the physic position of the axes (or rotation centre) and not those of the tool tip. If the system forecasts the limits exceeding, it activates a decelartion ramp to stop the program. bit 1-2-3 also activate (with value 1) the realtime vehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544rification of the operational limits for the “tool head” values in addition to the “physic positions” of the TCP. It is possible to select the TCP axis to check; bit 1 activates the first TCP linear axis verification, bit 2 activates it for the second and bit 3 for the third. bit 4-5-6 setting bit 0 to 0, controls of the pre-calculation operational limit are enabled for all the TCP axes (tool head values); to disable the control for some linear axes, it is possible to use these configuration bits. Bit 4 disables the control on the first linear axis, bit 5 on the second and bit 6 on the third. These bits will be used only when bit 0 (global enabling of the verification on the three axes) is set to 0 value.45004457K190

Prima Electro S.p.A.Type of manual4. 刀具和刀具补偿编程本章解释了如何对刀具和刀具补偿进行编程。 系统改进了控制器和刀具控制之间的接口，以及 T 和 M 字母的具体应用，RQT 和 RQP 功能的使 用. 关于 M 字母的进一步信息可以在第六章找到。4.1用于刀具编程的 T 字母该 T 字母给定了一个用于加工工序中的刀具和刀具补偿。 句法 http://www.wendangwang.com/doc/efe960bed681037ac6d62544T [tool], [.] [tool offset]其中： tool 特征: 两者参数范围的允许值从 0.0 到 999999999999.300。这个 15 位的数字的意义如下： 999999999999.300 刀具代号 r 刀具补偿代号 例如： 以下的例举行了不同的刀具编程和补偿编程方法。 T1 选择刀具 1 和在刀具表上被界定的刀具补偿。 是指刀具代号，是一个数字或者一个变量。 是指刀具补偿代号。其可以是一个数字或者是一个变量。 tool offsetT1.1 选择刀具 1 和刀具补偿 1。 T1.0 选择刀具 1，没有刀具补偿。 T.0 T0 T.1 从当前所用刀具中取消刀具补偿。 取消当前刀具和刀具补偿。 用当前所用刀具使用刀具补偿 1。45004457K191

Prima Electro S.p.A.Type of manual4.2用于多刀具编程的 T 字母该 T 字母给定了一个加工工序的刀具。 句法 T [master] [.] [tool offset] [/slave l] [first_slave, last slave]l variable, num_variables]其中： master是刀具代号。其可以是一个整数或者是一个局部或系统变量，在 0 到 999999999999 之间。tool offset是刀具补偿代号，与主刀具相关联。其可以是一个整数或者是一个局部或系 统变量，在 0 到 300 之间。slave first_slave是附属刀具代号数。其可以是是一个整数或者是一个局部或系统变量。 是一个刀具代号，代表一系列刀具中的第一个。其可以是是一个整数或者是 一个局部或系统变量。last_slave是一个刀具代号，代表一系列刀具中的最后一个。其可以是是一个整数或者 是一个局部或系统变量。variable num_variable是一个局部或者系统变量，包含了一系列刀具中的第一个。 是一个局部或者系统变量，代表变量数，从“variable”开始考虑。说明： 多刀具编程用于打孔的机器上。 与 T 编码相关的刀具管理http://www.wendangwang.com/doc/efe960bed681037ac6d62544是由机器 PLC 逻辑处理的，被编程了的刀具的值被送到此机器 PLC 逻辑。 用于附属的刀具编码的可编程值在 0 到 65535 之间变动。附属的刀具最大值是 60. 从 T 编码句法中你可以看到，被使用的刀具目录可以归于三种不同的格式： 1. 单一格式 例如： T1.2/ 50 T1.2 /20,33,45,46 刀具号 1, 50 补偿号 2 刀具号 1,20,33,45,46 补偿号 t 245004457K192

Prima Electro S.p.A.Type of manual2. 数字顺序格式 用按次序的编码可以简化多刀具的编程。 例如： T1.3 /[ 30, 35 ] T1.3 /[ 56, 51 ] T1.3 /[ 50, 52 ], [ 10,13 ] 相当于 T1.3 /30,31,32,33,34,35 相当于 T1.3 /56,55,54,53,52,51 相当于 T1.3 /50,51,52,10,11,12,13在第一个示例中，刀具编码是递增的次序，在第二个示例中，刀具编码是递减的次序。 3. 变量顺序格式 这个格式是基于变量的一个数列，刀具数从其中选择。 例如： E0 = 1, 30, 45 T1.2 / E0, 3  E0 = 1, 30, 45 SN0 = 4, 77 SN4 = 3 T1.2 / E0, SN4 ,  SN0,2  以上的三个格式可能混合。 例如： E0 = 29, 56 SN6 = 2 T1.3 /[ 7, 10 ], 15,  E0, SN6  E0, E1 依次载入 29, 56 SN6 被赋值 2 相当于 T1.3 /7,8,9,10,15,29,56 把 1, 30, 45 分别载入到 E0，E1，E2 相当于 T1.2 /E0, E1, E2 &amp; to T1.2 /1, 30, 45 E0, E1, E2, E3 依次载入 1, 30, 45 SN0, SN1 依次载入 4, 77 SN4 被赋值 3 相当于 T1.2 /E0, E1, E2, SN0, SN1 &amp; to T1.2 /1,30,45,4,774http://www.wendangwang.com/doc/efe960bed681037ac6d625445004457K193

Prima Electro S.p.A.Type of manual4.3h 字母h 地址允许把刀具补偿应用于点对点（G29）和连续的（G27-G28）方式中。 句法 h [tool offset]其中： tool offset 刀具补偿。是刀具补偿代号。其可以是一个整数或者一个在 0 到 300 之间的局部或系统变量。 说明： “h”字母在一个程序段中必须自己一行单独被编程。 “h”字母会覆盖“T”字母用 T 代码所激活的刀具补偿值。 刀具补偿所应用于的轴是用“T too.offset”命令编程了的轴。 当系统读取到了程序中的“h”值，便将补偿值应用于轴上。“h”不能与逻辑或者轴移动时同步。 如果“h”不同步，当其被加工程序读取时就会显示而不是在使用过程中。 同样的情况出现在同步使用“h”，就像 G96 中的。在这种情况下，“h”的应用必须与用于主轴旋 转的“#”同步来确保正确运行。 如果编程&quot;h&quot;时没有刀具补偿或者设定刀具补偿=0，则值用前一个&quot;h tool offset” 命令编程。该值可能通过一 个 RESET 命令复原。由机器逻辑来决定在 RESET 后是否应用补偿值。 如果机器逻辑没有正确处理，在同一个加工程序中为补偿使用&quot;h&quot; 和 T 将引起问题。推荐一次 只使用其中的一个方式。 用 h 地址编程的补偿值通常在储存 T 地址的地方显示。只有在刀具表的默认设置被使用时，补偿才能用一个 h。 补偿表的范围如下，补偿值从其中读取： Offset value Length 1 Length 2 Diameter Offset table fields Length 1   Current requalification length 1 Length 2   Current requalification length 2 Diameter   Current requalification diameter45004457K194

Prima Electro S.p.A.Type ohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544f manual例 1： ..... ..... ..... T[n].x ..... ..... hy ..... ..... 编程一个刀具和一个刀具补偿取消 X 刀具补偿，启用 Y 刀具补偿例 2： ..... ..... ..... hy ..... ..... T[n].x ..... ..... 取消由 h 启用的 Y 刀具补偿 启用 Y 刀具补偿例 3： ..... ..... ..... hx ..... ..... hy ..... 取消编程了的 X 刀具补偿，启用 Y45004457K195

Prima Electro S.p.A.Type of manual4.4TTR – 平头刀尖 Radius这个系统参数可以开启刀尖边缘半径管理功能，这些功能在使用了 球面刀尖 或者 平头刀尖时需要。 语法 TTR = value其中： value 数值，可以是 0 关闭该功能 1 启用该功能 NOTE The moment the tool corner radius management is enabled, the length 2 field (  requalification length and max. length) is used by the system to define the tool tip radius. In this connection, the length is no longer applied as a length corrector. The tool corner radius is used only within the TCP and the HSM for programming a T or an h.4.5AXO – Axis Offset DefinitionThis command makes it possible to associate the length offset values contained in the offset table to the machine axes. 语法 (http://www.wendangwang.com/doc/efe960bed681037ac6d62544AXO,[ [-] axis name1 ][, [-] axis name2])其中： axis name1name of the axis associated to length offset 1 in the offsets table. If the &quot;-&quot; sign is written before the name, the offset value is used with the inverse sign. If omitted, the length 1 of the offset is not associated with any axis. name of the axis associated to length offset 2 in the offsets table. If the &quot;-&quot; sign is written before the name, the offset value is used with the inverse sign. If omitted, the length 2 of the offset is not associated with any axis.axis name2说明： The default association between length offsets and characterised axes is made in the AXIS GENERAL INFO page of the AMP utility. This association can be changed with the AXO command. The preset values introduced in the offset tables always have a positive sign. The AXO command enables these values to be associated with axes bearing negative signs. The following are two examples of http://www.wendangwang.com/doc/efe960bed681037ac6d62544length offset values applied with and without AXO commands: Example 1: . . . N1 T1.4 M6 activates length 1 of offset 4 on the axis associated to length 1 in the offset characterisation phase. . .45004457K196

Prima Electro S.p.A.Type of manualN100 T0 M6disables the length offset value applied to the axis.45004457K197

Prima Electro S.p.A.Type of manualExample 2: . . . N1 (AXO,-X,Z) associates X to length offset 1 with negative sign and Z to length offset 2 with positive sign . . N50 T1.4 M6 applies length offset values 1 and 2 from offset 4 to axes X and Z as defined in the AXO command. Length offset 1 will be applied to the X axis with negative sign. . . N100 T0 M6 disables the length offset applied to axes X and Z. Example 3: . . N1 (AXO,,Z)associates the length 2 of the offset to axis Z.The system RESET command or the selection of a new part program re-establish the axis/offset defauhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544lt association characterised with AMP.4.6RQT – Requalifying Tool OffsetThe RQT command requalifies the length and diameter dimensions memorised in the offset tables. 语法 (RQT,tool,offset [,L..][,l..][,d..])其中： tool Is the tool number. offset Is the number of the offset to be requalified. The offset number is a value between 1 and 300. L l d Is the value to be added to offset length 1. Is the value to be added to offset length 2. Is the offset increment to be added to the diameter.说明： The values can be either numbers or contents in the variables. You must specify the length and diameter increments in the RQT command with the measuring unit configured in the system (inches or millimetres, G70/G71). These values cannot be associated to a scale factor (SCF). Examples: (RQT,10,1,L E40,d E41) This block requalifies tool 10, offset 1. The length 1 increment is contained in E40 and the diameter increment is contained in E41. (RQT,http://www.wendangwang.com/doc/efe960bed681037ac6d6254410,1,L E50,l E51) This block requalifies tool 10, offset 1. The length 1 increment is contained in E50 and the length 2 increment is contained in E51.45004457K198

Prima Electro S.p.A.Type of manual4.7RQP – Requalifying Tool OffsetThe RQP command requalifies and presets a specific tool offset according to programmed length and diameter dimensions. When the control executes this command, it writes the corresponding dimensions in the tool offset table by adding the specified length and diameter values. All the offset values are reset. 语法 (RQP,tool,offset [,L..] [,l..][,d..])其中： tool Is the tool number. offset Is the number of the offset to preset. It is a value between 1 and 300. The upper limit of the offset number depends on the number of records in the tool offset file. L l d Is the length increment to write to length offset 1. Is the length increment to write to length offset 2. Is the diameter incrementhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 to write to the offset field.说明： The values can either be some numbers or contents in the variables. You must specify the values of length and diameter increments in the RQP command with the measuring unit configured in he system (inches or millimetres, with G70/G71). These values cannot be associated to a scale factor (SCF). Examples: (RQP,10,1,L E40 ,d E41) This block presets offset 1 of tool 10. The value of length 1 is contained in E40 and the value of diameter is contained in E41.4.8TOU(TOF) – Tool Expiry DeclarationThe TOU command allows to declare the specified tool expired. 语法 (TOU,tool)其中： tool is the number of the tool number to be declared expired. It can be a local or a system variable Example: (TOU,5) E1=10 (TOU,10) ;Declares tool 5 in the tool table expired ; ;Declares tool 10 in the tool table expired45004457K199

Prima Electro S.p.A.Type of manual4.9LOA – Table LoadingThe LOA commahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nd allows dual port loading of the disk-resident table. 语法 (LOA, table name [.extension] [,par1] [,par2]])其中： table name extensionit is the file name of the table to be dual port loaded. it is the extension of the file name and refers to the type of table to be loaded: .TOL table of tools .OFS table of adapters .SPN table of spindles (for the WOOD option) .ORG table of origins .USR table of user variable .MAG table of magazines When there is no extension, the table referred to is the one pertaining to the Electronic Cam option (for description see relevant manual). When tool and adapter have been associated in the loading of the tools table, also the relevant strings are loaded automatically. The name of the table with its extension may also be defined by means of the variable SC. It is a parameter having a different meaning according to the type of table to be loaded: table of tools   par 1 stands for the number of magazine thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e tools belong to and it is compulsory when magazines are being used. table of origin   par 1 par1 is the number of the process to which the axes relevant to the origins to be loaded belongs to. It is considered only when loading the table tools together with the parameter par 1 and indicates whether the pocket values of the tools table need to be updated. par 2 = 0 no pocket update par 2 = 1 pocket update When no parameter is available, 0 is chosen by default.par 1par 2说明： The LOA command enables a dual port loading of the tables previously saved on file by TABLE EDITOR. The names for the relevant extensions which identify the type of table are given by default and can be different if modified through the SET UP utility of TABLE EDITOR. When using the magazines, the operation &quot;pocket initialization&quot; is to be accomplished by TABLE EDITOR. Such operation is necessary each time tables referred to magazines featuring dhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ifferent pockets are loaded or after reset of the dual port memory. Examples: (LOA, NEW_TOOL.MAG ) loads the magazine table named NEW_TOOL. (LOA, DRILL_T.TOL, 1, 1) loads the DRILL_IT tools table relevant to magazine 1 and updates the pocket field of each tool. (LOA, ORIG_http://www.wendangwang.com, 1) loads the ORIG_1 table relevant to process 1.45004457K200

5. 刀具直径补偿

刀具直径补偿是基于刀具的几何结构。典型的刀具部分横剖面是一个圆形，那么修正就需要用到刀具直径补偿。刀具直径补偿是垂直加工轮廓。下图显示了当刀具直径补偿应用时刀具是如何定位的.

[此处图片未下载成功]

path 编程路径

path 应用补偿时的实际路径刀具直径补偿的刀具的实际位置

下面是刀具宽度补偿，但其实它只不过是刀具直径补偿的另外一种形式。

[此处图片未下载成功]

图 2

5.1

语法

– 刀具直径补偿形式

(TTC, type [,cos(a),sin(a)]) (TTC)  相当于 (TTC, 0)

其中：

补偿形式：

(a),sin(a) 这是刀具和横坐标的夹角的正弦值和余弦值，如图所示。

这个向量的设定可以不设定，默认是0.0,1.1： vertical tool with the tip facing   bottom andhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 it can be used as a TCP alternative.

刀具直径补偿形式 1 刀具宽度补偿形式

这个参数可以在AMP里面设置作为默认设定。

[此处图片未下载成功]

Abscissa

parameters

如果仅仅是(TTC,0)或者(TTC)，表示两种形式均被取消。

系统遇到复位会恢复AMP设定值。

.2 G40 G41 G42 – 刀具直径补偿G代码

这些G代码能使刀具直径补偿失效或者启用：

取消刀具直径补偿

启用当刀具在轮廓的左边移动时的刀具补偿功能 G42 启用当刀具在轮廓的右边移动时的刀具直径补偿功能  句法

[G-codes] [operands] G41 [G-codes] [operands] G42 [G-codes] [operands]   其中： G-codes

启用刀具直径补偿

通过代码G41和G42来启用刀具直径补偿。

在轮廓中的第一个点，刀具直径补偿是垂直第一个直线或者圆弧的移动，该移动是在当前激活平面上编写了G41和G42后作用的。

下面的示例显示了刀具直径补偿是如何应用的。

开始是直线移动的示例

[此处图片未下载成功]

其它与G41, G42和G40兼容的G代码（见第一章中的“兼容的G代码”表）。 任何在G字母程序段允许的操作数或代码。

程序：

刀具在轮廓右边的刀具直径补偿： G1 G42 X-50 Y15 F200 X-20 Y45

刀具在轮廓左边的刀具直径补偿： G1 G41 X-50 Y15 F200 X-20 Y45

开始是圆弧移动的示例

[此处图片未下载成功]

://www.wendangwang.com/doc/efe960bed681037ac6d62544程序：

刀具在轮廓右边的刀具直径补偿：

G42 X-31.622 Y40 F200 G2 X33.541 Y35 I J25 G1 X.....

刀具在轮廓左边的刀具直径补偿： G1 G41 X-31.622 Y40 F200 G2 X33.541 Y35 I J25 G1 X....

Thickness Compensation  (TTC, 1)

system determines the tool direction along the machine plane activating the compensation with G41 and G42. The programmed profile is compensated according to the direction.

the TTC is 未使用, the programmed tool direction is considered as vertical, but if TCP is active, the direction is calculated according both to the position of the rotary axes and  to the configuration.  Machine plane (might be rotated using the UPR) is described by plane definition codes (G16, G17, G18, G19); the system calculates the tool direction on the plane along which the grindstone thickness offset is applied.

tool centre will run (on the left if programmed G41 or on the right if G42) a distance equivalehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nt to half of the disc thickness according to the vertical tool and to a programmed point within the coordinates of the part. if the tool is not vertical, the behaviour will be similar, but the move will be along the direction perpendicular to the tool direction.

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

In the case of a linear element perpendicular to the tool direction, the programmed point

will be along that a direction and the direction does not depend on G41/G42, but is opposite to the element direction. Let’s assume:

Direction

controlled point

&#176; contact point between

tool and the workpiece

&#176; contact point between the tool and the part

controlled point

is performed on the plane using a fixed disc inclination, therefore, during G41 or G42 and G40, disc inclinahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544tions contemporary to the linear axes moves can’t be forecasted. If the tool inclination has to be changed, the compensation section has to be previously closed by G40.

:

first profile movement is linear

the disc thickness compensation, a linear element is transformed in another actor translated according to its direction, to the tool direction and in some occasions according to the mirror as well.

[此处图片未下载成功]

:

thickness compensation on the right of the profile: TTC = 1

G42 X-50 Z15 F200 X-20 Z45 X10 Z15

thickness compensation on the left of the profile: TTC = 1

G41 X-50 Z15 F200 X-20 Z45 X10 Z15

first profile movement is a circle

the disc thickness cmpensation, a circular element is resolved in one or more parts if the tanget tool point (PT) to the circle is internal or exterhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nal to the arc limits Pi e Pf (图3).

- PT  external:  the system creates only the first circle having its centre in c’. The circle is determined by

translation of c equal to the cutter radius oriented in the direction required and having the same radius of the non-offsetted circle.

- PT  internal:  the system created the aforementioned circle, the line passing through PT and tangent to

circle only if the compensation is external. In this case, the system generates a second circle having its centre in c’’ with a translation opposite to the first and with the same radius.

PT matches one of the two extreme arc points (Pi o Pf), system creates an arc with a tangent in PT.

[此处图片未下载成功]

Prima Electro S.p.A.

of manual

G41

5 0 15 65 115 X c’ Pi c c” Pf

K

[此处图片未下载成功]

://www.wendangwang.com/doc/efe960bed681037ac6d62544am:

thickness compensation on the right of the Disc thickness compensation on the left of the profile: profile: TTC = 1 TTC = 1 G1 G42 X15 Z5 F200 G1 G41 X15 Z5 F200 G2 X115 I65 J5 G2 X115 I65 J5 G1 X..... G1 X.....

on using tool compensation

enabled, tool compensation is applied to all the moves programmed at machining or rapid feedrate. After tool compensation has been enabled by G41 or G42, the following G functions cannot be programmed:

[此处图片未下载成功]

[此处图片未下载成功]

G81 - G89 (canned cycles)

[此处图片未下载成功]

G70 - G71 (mm/inch programming)

[此处图片未下载成功]

G79 (programming referred to machine zero)

[此处图片未下载成功]

G33 (threading)

[此处图片未下载成功]

G72 - G73 - G74 (measuring cycles)

- G17 - G18 - G19 (change of interpolation plane)

tool compensation is active, the control http://www.wendangwang.com/doc/efe960bed681037ac6d62544displays an error signal if:

[此处图片未下载成功]

[此处图片未下载成功]

the programmed internal radius is shorter than the tool radius.

execution of a compensated linear move would reverse the tool direction with respect to the original profile.

a profile compensated with G41 or G42 you can program up to six consecutive movements of axes that are not on the profile.

刀具路径最优化(TPO)

刀具路径优化(TPO) 可以从加工程序或者用MDI来启用。

该功能通过TPO系统变量来编程，也可以配合TPT系统变量来迎合特定的应用要求。 TPO 允许界定两种优化模式：

刀具路径在两个直线或者圆形的程序段之间的拐角处处自然“合拢” 向轮廓的横切/退出转向 （在一个圆形的弧线）    TPO 和TPT会在本章的后面详述。

取消刀具直径补偿

代码可以取消刀具直径补偿。刀可能如下例所示退出：

[此处图片未下载成功]

如果TPO没有启动（标准补偿模式），G40所在的程序段的运动被认为是仍然采取刀具直径补偿；

[此处图片未下载成功]

如果TPO启动，G40所在程序段的运动被认为是不采用刀具直径补偿。

这些选项在下面的示例中说明。

[此处图片未下载成功]

在轮廓中的最后一个运动是直线的情况(TPO=0)

[此处图片未下载成功]

[此处图片http://www.wendangwang.com/doc/efe960bed681037ac6d62544未下载成功]

在轮廓中的最后一个移动是圆形的情况(TPO=0)

程序：

G2 G40 X36.62 Y40 I J25 N100 G X.. Y..

[此处图片未下载成功]

程序：

G1 G40 X50 Y15 N100 G X.. Y..

启动TPO取消刀具直径补偿

启动TPO时，刀具直径总是通过G40补偿；与标准步骤的唯一区别是最后一个程序段是如何执行的。 这些选择项在下面的示例中说明。

[此处图片未下载成功]

轮廓中的最后一个移动是直线的情况(TPO 启动)

[此处图片未下载成功]

程序：

G1 X20 Y40

G1 G40 X50 Y15 N100 G X.. Y..

[此处图片未下载成功]

轮廓中的最后一个移动是圆形的情况(TPO 启动)

[此处图片未下载成功]

程序：

G1X-33.541 Y35

G2 G40 X36.62 Y40 I J25 N100 G X.. Y..

your release is earlier than 3.0 you must check whether G40 is programmed in your old part programs. When TPO is active, G40 exits from cutter diameter compensation somewhat differently.

you program a block including only G40 (i.e. not associated to any final point), you will http://www.wendangwang.com/doc/efe960bed681037ac6d62544obtain the same result you would with standard diameter compensation (TPO=0).

to writing a program read this section and the descriptions of TPO and TPT carefully.

[此处图片未下载成功]

disc thickness compensation

disables the disc thickness compensation. No matter the TPO status, exit mode is standard (that means the move programmed on G40 is still in offset mode) .

examples show several cases of profile exit:

[此处图片未下载成功]

last profile motion is straight

[此处图片未下载成功]

Program:

G1 G40 X50 Z15 N100 G X.. Z..

[此处图片未下载成功]

last profile motion is a circle:

:

G1 G40 X50 Z95 N100 G X.. Z..

:

G2 G40 X86.6 Z50 R100

G X.. Z..

.3 5.4

[此处图片未下载成功]

[此处图片未下载成功]

86.

刀具直径补http://www.wendangwang.com/doc/efe960bed681037ac6d62544偿改变

这一部分描述补偿类型的改变(G41 --&gt; G42，反之亦然)在补偿轮廓加工中是如何处理的。补偿类型的改变可能在编程路径的交叉点（左/右或右/左补偿）或在系统自动加入一个新的移动程序段时出现。

补偿改变的类型（在交叉点或用加入的连接程序段）取决于之前移动的类型和之后移动的类型。在以下的几页中会讨论各种不同的可能性：

[此处图片未下载成功]

直线的/直线的，带切线的移动程序段

[此处图片未下载成功]

直线的/直线的，反向

[此处图片未下载成功]

直线的/直线的，带新移动程序段的自动生成

[此处图片未下载成功]

直线的/直线的且没有新移动程序段的自动生成

[此处图片未下载成功]

直线的/圆形的 – 圆形的/直线的

[此处图片未下载成功]

圆形的/圆形的

直线的/直线的刀具路径

下图是在两个直线类型移动的执行中，当补偿从G41改变到G42，刀具路径的说明。 从G41到G42的改变，控制器会生成两个点，这两个点称为point 1 和point 2。

[此处图片未下载成功]

1是刀具在补偿类型改变前的最后位置。

[此处图片未下载成功]

2是启动第一个使用改变的补偿方向的程序段的期望起点。

控制器自动生成移动程序段使point 1 与 point 2连接：

[此处图片未下载成功]

[此处图片未下载成功]

point 1

直线的/直线的改变，带正切的移动程序段

Compensated

Programmed in G42

直线的/直线的改变，带方向倒置://www.wendangwang.com/doc/efe960bed681037ac6d62544r

[此处图片未下载成功]

pathProgpath

2

直线的/直线的改变，带新程序段的生成

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

直线的/圆形的，圆形的/直线的，圆形的/圆形的刀具路径

下面每一类型的刀具路径，其中有补偿方向改变的发生，10系列系统将尝试在G41中编程的路径和G42中编程的路径之间找到一个交叉点（反之亦然）。

如果10系列找到一个交叉点，它将修改原来补偿的刀具路径的终点，而且新补偿的刀具路径的起点将和这个交叉点一致（见下图）。

G42

G41Progpath

补偿改变及当前路径的交叉点

然而，在刀具路径之间没有交叉点的情况也可能出现；在这种情况下，系统从G41转变到G42（反之亦然）将会如下图所示工作。

1是刀具补偿类型改变前的终点

2是启动第一个使用改变的补偿方向的程序段的期望起点。

控制器自动生成移动程序段使point 1 与 point 2连接：

1

[此处图片未下载成功]

补偿改变且刀具路径之间没有交接点

5.5

– 补偿轮廓中的半径

当加工凸面的轮廓，你可能在几何图案成分之间要一个圆弧。  句法 r value   其中：

将被编程的半径。顺时针方向的移动，编http://www.wendangwang.com/doc/efe960bed681037ac6d62544程一个负值的半径；逆时针方向的移动，编程一个正值。

[此处图片未下载成功]

[此处图片未下载成功]

编程r0 (半径等于0)会引起刀具中心跟随一个圆形的弧形，其中心在轮廓角。  示例：

没有半径

) N20 G1 X100 Y100 2) N21 X-100

带半径 1)  N20 G1 X100 Y100  N21 r0 2)  N22 X-100

.6 b – 补偿轮廓上的斜面

在b地址后编程一个不带符号的值，你可以插入一个斜面，而不是一个在两个直线的或者圆形的移动程序段之间的半径，这些程序段可生成交叉路径。  句法 b value   其中：

是从交叉点测得的斜面长度。

该b值可能有如下几种解读：

[此处图片未下载成功]

在两个直线轮廓间的斜面：b是在延长的轮廓部分之间，从生成的终点到理论上的交叉点的距离。

[此处图片未下载成功]

在一个直线和圆形轮廓间的斜面：b是在直线轮廓的延长部分之间，从理论上的交叉点到到圆形轮廓的

示例：

[此处图片未下载成功]

正切的距离。

[此处图片未下载成功]

在两个圆形轮廓间的斜面：b是在正切的延长部分之间，从理论上的交叉点到圆形轮廓的距离。

在两个直线程序段之间的斜面

编程示例：  .  .

G1 X10 Y100     ;block 1 N11 b3

X-100                ;block 2  .  .

在圆形和直线移动程序段之间的斜面

Programming example:编程示例：

.

GXY N11 G42

://www.wendangwang.com/doc/efe960bed681037ac6d6254412 G1X10Y70F1000 N14 G2X70Y20R50

;block

b10

G1X150Y90 ;block 2 N20 G40 . . .

[此处图片未下载成功]

POINTPROGRAMMED

编程示例：  . N20 G42 N22 GXY

N26 b10

N30 G40  .  . 在两个圆形移动程序段之间的斜面

[此处图片未下载成功]

编程示例  .  . N10 G42

GX10Y60

G2X50Y40R50F1000 N40 b5

G2X100Y5050R30  .  .

;block 1 ;block 2

.7 TPO – Path optimisation on bevels with G41(G42

(Tool Path Optimisation) allows to optimise the tool path when G41 or G42 are active.

algorithm automatically introduces circular interpolations at profile start and end, and linear or circular radiuses on the profile bevels.  语法

= n

其中： n Optimisation mode. Allowed values are:  The value to be specified for n in the instruction is obtained from the sum of the decimal weights  corresponding to each of the features deshttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ired.  If n = 0 the optimisation algorithm is disabled.

linear radiusing movements between the elements

/exit  tangent to profile

profile inversion with triliterals GTP and CCP

[此处图片未下载成功]

Activates the algorithm for maintaining the

speed constant in G41/G42

circular radiusing movements between the elements

[此处图片未下载成功]

circular radiusing movements on internal bevel

说明：

block programming the TPO=n instruction activates the tool optimisation algorithm.

algorithm can automatically introduce movements at the beginning/at the end of the profile and it can optimise the path on corners. Depending on the profile, the algorithm automatically introduces from 1 to 3 optimisation moves.

is ignored in a GTL program.

://www.wendangwang.com/doc/efe960bed681037ac6d62544 power up the system is enabled with the TPO mode configured in AMP. This optimisation mode may be altered from the program.  RESET restores the mode configured in AMP.

activation of bit 5 and/or of bit 6 works only if bit 0 is enabled too, i.e. when you want to introduce a circular radius in lieu of a linear one, set TPO = 33.

you want to introduce a circular radius on the inner corners of a profile, set TPO = 65

=1, TPO=33 and TPO=65 Modes

TPO=1 activates the tool path optimisation algorithm by introducing linear radiusing movements between the profile elements as a function of the angular deviation between the elements themselves. Furthermore, if bit 5 has been set too (TPO=33), then, provided that the conditions for corner optimisation are met, through the introduction of linear movements a circular radius is introduced, having its centre at the intersection of the http://www.wendangwang.com/doc/efe960bed681037ac6d62544two non-compensated elements and a radius corresponding to tool radius.

bit 6 is active too (TPO= 1 32 64=97), the above considerations are applied to the inner corners.

cases of application of the algorithm are as follows: A) Right angle-right angle with angle beta of deviation between 0&#176; and TPA (0&#176; &lt;   &lt;

&#176;), with variableTPA, which is set by default on 90&#176;

-right angle, right angle-circle, circle-circle with angle of deviation between 0&#176;

)

180&#176;  (0&#176; &lt;   &lt; 180&#176;).

either a bevel (b) or a radius (r) has been programmed between the elements described in A) and B), the algorithm is not applied.

:

this example,   is smaller than 90&#176;

[此处图片未下载成功]

Without optimization (TPO =0)

optimization (TPO=1)

[此处图片未下载成功]

[此处图片未下载成功]://www.wendangwang.com/doc/efe960bed681037ac6d62544r

optimization (TPO=33)

optimization (TPO=65)

that in the above examples the TPT threshold has been ignored, as if TPT=0.

figure below illustrates the strategy of TPO when TPT is not zero, i.e., a threshold deviation from the corner is programmed:

the case of an outer corner, the afore-mentioned circular radius will have its centre translated according to the same calculation criteria as are used for linear radiuses, and the radius will be reduced accordingly.

the case of an inner corner, the radius of the circular radius is calculated so as to have the tool path deviate from TPT by the amount that would be obtained without the introduction of the radius

a disc thickness compensation case (TTC,1) the junction is inserted with TPO=33 exceeding the angle of a quantity not depending on the TPT, but on the distance between the angle and the othhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544er compensated elements.

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

Examples of profile optimisation with TPO=1

these profiles the angle deviation requires an optimisation algorithm.

[此处图片未下载成功]

[此处图片未下载成功]

Angles from 0&#176; to 90&#176; formed by two straight lines

[此处图片未下载成功]

[此处图片未下载成功]

Angle from 0&#176; to 180&#176;

by a circle-straight line intersection

of profiles where algorithm introduces optimization moves

these examples the algorithm recalculates the profile and introduces from 1 to 3 optimisation moves between bevels.

) Line - line

[此处图片未下载成功]

The algorithm generates 1 move

) Line - circle

[此处图片未下载成功]

algorithm generates 2 moves

) Circle - line

[此处图片未http://www.wendangwang.com/doc/efe960bed681037ac6d62544下载成功]

algorithm generates 2 moves

generated

[此处图片未下载成功]

) Circle - circle

algorithm generates 3 moves

=2 mode

=2 enables an infeed/exit algorithm that keeps the tool tangent to the profile by introducing circular elements at profile start and end.

profile infeed the algorithm generates a circle between the first point of the offset profile (P1) and the preceding point (P0). The first point is the one programmed in the G41 or G42 block.

: ..... X80 Y70  ;P0 G41 X100 Y100 ;P1 X140   ;P2 .....   ;etc. …..

profile exit the algorithm generates a circle between the last point of the offset profile (P99) and the last point of the exit element in the profile (P100). The exit element is programmed in the G40 block.

: .....

X100 Y100 ;P1 ….. ..... ....http://www.wendangwang.com/doc/efe960bed681037ac6d62544. .....

Y160  ;P99 G40 X180 Y185 ;P100 .....   ;etc. ..... …..

=3 mode

=3 simultaneously enables TPO=1 and TPO=2 algorithms, which allows to introduce both radiuses between elements and circular moves at profile start and end. The rules defined for TPO=1 and TPO=2 also apply to TPO=3.

Examples of TPO=2 mode

1:

[此处图片未下载成功]

52,5

,5

,5

N2 N3 N4 N5 N6 N7 N8

M3 T1.1M6 X5 Y5

G42 X15 Y15 F500 X30 X40 Y30 X32.5 Y42.5

X32.5 Y52.5 GX100

;tool radius = 2.5

;first point in the profile

;last point in the profile

[此处图片未下载成功]

N1 N2 N3 N4 N5 N6 N7 N8 N9

M3 T1.1 M6 X0 Y0

G41 Y15 F800 X -20 Y45 X40 Y15 X0

Y0

;tool radius = 2.5

;first point in the profile

;last point in the profile

The TPO=4http://www.wendangwang.com/doc/efe960bed681037ac6d62544 mode activates the profile inversion algorithm.

feature permits machining of a profile starting from the last movement, and finishing on the first (reverse machining).

[此处图片未下载成功]

This feature in managed in connection with commands GTP and CCP only.

algorithm also provides for inversion of any offset modes, so as to maintain

[此处图片未下载成功]

position of the inside/outside tool as required.

further details, see the pages dealing with the triliterals GTP and CCP (page 4-37 and 4-40).

=8 and TPO=16 modes

=8 and TPO=16 modes activate the algorithm that keeps the machining speed in G41/G42 constant. In particular, the speed of contact between the tool and the part is kept constant, varying the feed rate with reference to the centre of the tool.

variation is a function of the tool radius and is only applied to circular movementhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544s. It will produce an increase or decrease in the feed rate with reference to the centre of the tool depending on whether the radius of the circle moved by the centre of the tool is greater or less than the radius of the programmed circle. The feed rate is increased by setting bit 3 of variable TPO (TPO=8) while it is decreased by setting bit 4 (TPO=16).

3 and 4 of TPO may be set together and even at the same time as all the other bits of the same variable to enable the corresponding features.

=32 mode and 64 mode

the same as having programmed TPO = 0.

is so because the activation of external and inner bevel optimisation through the introduction of a circular radius requires the prior programming of TPO = 1. If bit 0 = 0 and bit 5 and/or bit 6 = 1 (TPO=32 and/or TPO=64), the optimisation algorithm by means of circular radiuses is not enabled.

5.8 TPA – Threshold angle for TPO://www.wendangwang.com/doc/efe960bed681037ac6d62544variable that consists of the threshold angle within which two linear elements can be radiused in tool compensation mode (G41/G42).  语法

= value

其中：

Threshold angle expressed in degrees. If the angle between two adjacent elements is smaller than  the value of TPA, a circular or linear radius is introduced in accordance with the values set in TPO.  The default value of TPA is = 90&#176;; this value can also be configured in AMP.  If the value has been changed by the program, RESET restores the default value.

variable has been introduced to be able to configure the threshold angle used by the Tool Path Optimisation (TPO) algorithm to radius two linear elements in tool compensation mode: so far, this angle was fixed at 90&#176;. If at least one element is circular the optimisation algorithm remains unvaried, i.e., a radius (either linear or circular, dependinghttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 on the value of TPO) is introduced regardless of the angle between the two elements.

:

TPA &gt; 90&#176; and TPO = 1

[此处图片未下载成功]

With TPA &gt; 90&#176; and TPO = 33

[此处图片未下载成功]

5.9 TPT – Tool Path Threshold

instruction specifies a threshold for bevels during tool path optimisation when TPO=1.

语法

= value

其中：

Threshold expressed in the default unit of measure (mm/inch). It represents the distance between  the tool cutter and the bevel generated by the programmed profile. It can also be configured in  AMP.

:

[此处图片未下载成功]

[此处图片未下载成功]

说明：

threshold programmed with TPT will be ignored by the system if it takes the mill centre beyond the theoretical point obtained through standard tool diameter compensation (G41/G42 without TPO programming).

this case thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e TPO algorithm will be temporarily disabled, G41/G42 will be applied without TPO and there will be no error signal.

:

TPO algoritm

[此处图片未下载成功]

Normal deviation from41

.10 u v w – Paraxial Compensation

compensation factors u,v,w are programmed in a block, the axes position to a point whose

are equal to the programmed coordinates plus the product of the cutter radius by the compensation factor (u, v, w):

position = programmed X   (cutter radius * u)

position = programmed Y   (cutter radius * v)

position = programmed Z   (cutter radius * w)

compensation factors are used both for extremely simplified profiles (contouring parallel to axes) and three-dimensional milling surfaces. You cannot use the u,v,w factors when the control is in cutter diameter compensation mode (G41-G42).

factors u,v,w are negative, thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ey must be followed by a minus sign. If they are positive, the plus sign can be omitted.

order to determine the value and the sign you must consider paraxial factors u,v,w respectively as the X, Y, Z coordinates of the profile vertex corrected by a unit. X, Y and Z are referred to a system of cartesian axes that are parallel to the axes of a machine whose origin is represented by the point to be compensated.

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

the sign of u, v, w compensation factors

unit vector represents a cutter radius offset that is one unit long; the control, the increments of translation are the product of the u,v,w values multiplied by the cutter radius.

can compensate profiles that consist of:://www.wendangwang.com/doc/efe960bed681037ac6d62544arline segments parallel to the axes or forming an angle with the axes  straight line segments and arcs tangent to the straight lines

arcs (provided they are still tangent to one another after they have been translated on a parallel path).

u,v,w factors are only valid in the block in which they are programmed. They are used by the control only if they are associated to the corresponding coordinates:

for the 1st configured axis (typically X)  v for the 2nd configured axis (typically Y)  w to the 3rd configured axis (typically Z).

of compensation factor applications u, v, w

:

:

T1.01 M6 S. . F. . N6 G X Y30 N7 G1 Y10 v1 N8 X40 u-1 N9 Y30

G X. . Y. .

2:

: N13 G X Y N14 G1 Z-10

X-20 Y-20 u1 v1 N16 X20 u-1 N17 Y20 v-1 N18 X-20 u1 N19 Y-20 v1 N20 G X Y

://www.wendangwang.com/doc/efe960bed681037ac6d62544arExample 4:

:

G X-35 Y-35 N14 Z-10

G1 X-20 Y-20 u-1 v-1 N16 X20 u1 N17 Y20 v1 N18 X-20 u-1 N19 Y-20 v-1 N20 GZ

[此处图片未下载成功]

[此处图片未下载成功]

[此处图片未下载成功]

Program: N12 . . .

G X-30 Y N14 G1 Y20 v-1 N15 X30 N16 Y-20 v1 N17 X-30 N18 . . .

6:

[此处图片未下载成功]

:

G X40 Y B0 N13 G1 X30 u1 N14 X25 B360 u1 N15 G X40

5.11 UVW – Definition of axes for paraxial compensation

is possible to change the axes on which paraxial compensation is performed. As a rule, paraxial compensation is applied, within each process, on the first three axes configured (the first three to appear on the screen). With triliteral (UVW) you can change the axes on which paraxial compensation is performed.

语法

(UVW, axis1 axis2 [axis3])

其中：

…axis3  http://www.wendangwang.com/doc/efe960bed681037ac6d62544are the names of the axes to be associated with the uvw paraxial compensation:    axis 1 is associated with parameter u, axis 2 with parameter v, and axis 3 with    parameter w..

说明：

only two axes are specified in the command, the paraxial compensation will be activated only for parameters uv, and the third parameter (w) will be ignored.

defined, the association between the axes and the uvw parameter remains active until the next RESET; then the default association (the first three axes configured) is restored. A GTA command and the activation of a virtualisation (UPR, UVA, UVP…) will also restore the default association, unless all the axes (construed as axis ID) on which the uvw parameters are active remain present even after the execution of the command.

:

(UVW,XYZ)  N20 h1

X10u1Y20Z40

(UPR,XYZ,PQD,20,20,0)     N50 (DAN,XP,YQ,ZD) N60 (UVW,XYZ)  in XYZ)://www.wendangwang.com/doc/efe960bed681037ac6d62544arX10u1Y20v0.3Z40w0.3 N80 (UPR,XYZ,PQD,0,20,20)     N90 X0u1Y5v0.50Z4w-0.5

uvw on X Y and Z respectively

UPR, the uvw parameters are activated on the first three axes configured

the uvw parameters on PQD (the DAN has renamed them

a new UPR, the uvw are maintained on PQD  because these are still present

5.12 MSA (UOV) – Defining a Machining Stock Allowance

MSA command defines the value of the machining stock allowance along the profile. It is used in roughing and pre-finishing cycles. MSA can be programmed in a block, assigned in an MDI or entered via softkey.  语法

= value

其中：

It can be a decimal number or an E parameter. It is programmed in the same measuring unit (G70- G71) that is currently active in the program.

:

system uses the programmed MSA to calculathttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e the offset value to be applied to the profile when cutter diameter compensation (G41 or G42) is active.

offset value is the sum of the tool radius and the MSA.

:

= 0.5  Assigns a 0.5 machining allowance E30  = 1.5 MSA  = E30  Assigns a 1.5 machining allowance

Contour Milling

automatic contour milling commands (GTP and CCP) are designed for machining of profiles with radius compensation (G41/G42), generally defined using graphic tools.

graphic tools (e.g. the Graphic Editor option) translate the drawing of the part to be machined into a technological program written in elementary ISO language.

of the main characteristics of this feature is that the profiles for machining are seen as subprograms.

profiles must be defined on a plane (e.g. XY) and can only contain the G operators for movement type (G1, G2, G3).

[此处图片未下载成功]

://www.wendangwang.com/doc/efe960bed681037ac6d62544arThe contour milling commands will do the following:

determine an approach point off the profile;

[此处图片未下载成功]

machining as described in the subprogram;

[此处图片未下载成功]

rotation, taking the first point of the profile as the rotation origin;

[此处图片未下载成功]

machining, starting from the last element of the subprogram through to the first (reverse machining).

all cases, approach with compensation is scheduled on the first point of the profile (first block of program with abscissa/ordinate movements).

Limits to use of automatic contour miling

limits regarding use of automatic contour milling are as follows:

[此处图片未下载成功]

profile must be described in full in a subroutine, indicated previously by profile name.

[此处图片未下载成功]

profile shall be cohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nsidered closed if the first point described in the part program subroutine coincides with the last.

[此处图片未下载成功]

correction (offset_mode) will be activated automatically on the first block of the subroutine and de-activated on the last block.

[此处图片未下载成功]

blocks of the subroutine must be exclusively ISO type, programming of the following is

[此处图片未下载成功]

allowed:

[此处图片未下载成功]

Axis names [dimensions]

movement functions (G1, G2, G3

[此处图片未下载成功]

with possibly their operands)

-letter commands in general shall NOT be taken into consideration (during the  profile analysis stage), especially any commands that could modify the description of the  profile (origins, mirror, scale factor).

:

to respect these indications may lead to incorrect interpretation of the profile descrhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ibed in the subroutine.

5.13 GTP – Get Point

the approach point off the profile.

语法

(GTP, profile_name, offset_mode, E-par, approach_type, angle)

其中：

_name offset_mode

-par

_type

ASCII string representing the name of the part program that the profile is described in.

values are 0, 1, 2.

the tool diameter offset mode to be used:   0 = no offset   1 = offset with tool on left of profile   2 = offset with tool on right of profile

variable in which the coordinates of the approach point calculated by the system will be loaded:   index            abscissa   index 1        ordinate

values are 0, 1, 2, 3.

the type of external approach to the profile; a different calculated point corresponds to each code (see next page).

of rotation:

://www.wendangwang.com/doc/efe960bed681037ac6d62544presents the value of the rotation angle with which the profile will be executed.

[此处图片未下载成功]

NOTES:

distance between the external approach point to the profile and the machining starting point is determed on the basis of the value in system variable MSA.

[此处图片未下载成功]

is possible of a feature that inverts direction of motion of the profile using system variable TPO (TPO=4 profile inversion)

further details of the TPO coding values see page 4-17.

you program offset_mode=0 , the approach_type is forced to “1” (approach tangential to

) without any further indications from the system.

Determining the approach point

_type=0

occurs perpendicular to the first element of the profile. The approach will be linear or

, depending on value of the variable TPO.

://www.wendangwang.com/doc/efe960bed681037ac6d62544icular approach to profile

[此处图片未下载成功]

_type=1

occurs tangential to the first element of the profile. The approach is always linear.

approach to the profile

approach_type=2

occurs on the

between the first and last points of the profile; the

will be linear or circular, depending on value of the variable TPO.

on intersection of first and last point of the profile.

[此处图片未下载成功]

_type=3

ocurs on the bisector of the angle formed by the movements generated with approach_type=0 and approach_type=1;  the approach will be linear or circular, depending on the value of the variable TPO.

on bisector

[此处图片未下载成功]

(tangent)

Prima Electro S.p.A.Type of manual5.14CCP – Cutter Compensation Profilehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544Performs contour milling of a profile, with tool diameter compensation. 语法 (CCP, profile_name, offset_mode, exit_type, angle) 其中： profile_name offset_mode exit_typeAn ASCII string representing the name of the part program the profile is described in. Possible values 0, 1, 2. Represents the offset mode with which machining is performed. Possible values 0, 1, 2, 3. Identifies the type of exit from the profile; a different calculated point corresponds to each code. Angle of rotation. Determines the value of the rotation angle the profile will be executed with.angle说明： The point of exit off the profile is determined by considering a value, seen as the safety distance. This value, associated with the exit point type, determines position on the plane of the exit point taken from system variable MSA. NOTE: Activation is possible of a feature that inverts direction of motion of the profile using system variable TPO (TPO=4 profile ihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544nversion active). For further details of the TPO coding values see page 4-16.45004457K241

Prima Electro S.p.A.Type of manual6. 主轴的编程在这章所描述的字母必须由机器逻辑来管理。主轴字母 用 G96/G97，S 地址来编程主轴速度—rpm，或者作为固定表面速率（即线速度）。此外，一些 M 字母影响 主轴开关状态和范围等等。6.1G96 G97 – CSS 和 RPM 编程以下 G 代码控制主轴速度编程。 G96 G97 句法 G97 [G-codes] [operands] G96 [G-codes] [operands] 速度编程，恒定的表面速度即线速度，英文缩写为 CSS。 速度编程，转/分钟，英文缩写为 RPM。其中： G-codes operands 特征: G97 编程以 rpm 为单位激活 S 编程。G97 是控制器的默认模式。 G96 激活 S 字母的固定表面速度（即 CSS）编程，单位为英寸每分(G70)或米每分 (G71)。G96 使主轴速度由 直径轴的位置控制，以保持主轴速度在加工表面不变。 当 G96 运行时，直径轴的位置视作为半径，恒定表面速度(S)为其编程。G96 同 G97 是同一模态，相互会覆 盖。 在 G96 期间改变 S 字母指令。取消 CSS 模式 如果当 G96 在运行时，你想改变 S 字母的值，控制必须处于 G00 或 G29 模式。要取消 G96CSS，控制器必须 处于 G00 模式且程序段带 G97 和定义主轴（rpm）S 字母的值。 示例： 下面的示例说明了 CSS 编程。 假定上电后激活的 G 代码: G00, G27, G70, G95, G97 假设最大转数为: 800 转/分钟 其它与 G96 和 G97 兼容的 G 代码（见第一章的“兼容的 G 代码”）。 任一可以用在 G 字母程序段的操作数或代码。45004457K242

Prima Electro S.p.A.Type ohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544f manualN1 G90 G00 N3 U5 N4 SSL=700 N5 G96 S400 M3 N6 G1 U0 Z -2 F10 N7 U5 Z0 N8 G00 N10 G00 N11 N12 N13 N14 ;预设直径轴 U ;限制主轴转速上限为 700 转/分钟 ;固定表面速度为 400 尺每分钟 ; ;准备改变主轴转速 S ;准备取消 G96N9 G01 S300 U0 Z-2 ;新的固定表面速度为 300 尺每分钟 G97 S100 ;启用 G97, S=100 rpm G01 Z0 ; U5 G00 ; ;刀停止 ;程序结束 S operators cannot be programmed when the process is on hold.N15 M05 N16 M026.2 6.3 SSL – 主轴速度限制SSL 命令，通过 G96 来设置在 CSS 期间主轴允许的最大转速– rpm。 句法 SSL=value其中： value 示例： SSL = 2000 E32 = 1500 SSL = E32 说明： 当直径轴越靠近主轴中线时，主轴要增大转速才能维持恒定的表面速度 S。SSL 命令限制主轴转速不能高于某 个值，这个限制值应该要低于最大的转速值。 SSL 命令必须在 S 字母语句之前被编程（G96）。 指定一个 2000rmp 的主轴速度限制 指定一个 1500rmp 的主轴速度限制 是可以直接用一个小数或者用 E 参数间接编程的值。确定在使用 G96 程序段前，输入这个命令语句。45004457K243

Prima Electro S.p.A.Type of manual6.4M19 - Oriented Spindle Stop M19 – 指定方向的轴停止通常，M19 字母用一个预设的角度让主轴停止。该特征在退出孔口平面操作中很便利，因为其允许定位主轴 停止时候轴的静态旋转角度，移动 X 或 Y 轴（取决于刀片方向），进到孔里面，然后再重新定位主轴，然后 开始加工。 在钻孔的操作中，M19 可以被用于提升精度，来避免在 Z 轴返回移动时刮伤镗过的http://www.wendangwang.com/doc/efe960bed681037ac6d62544表面。在这种情况下，你 可以完成穿孔，确定主轴的方向，根据刀片的方向移动 X 或 Y 轴，来执行 Z 轴的返回。 M19 可以通过 M03, M04, M13, M14 来取消。当控制器在程序段中（该程序段同样包含移动信息）读取 M19 时，M19 先于程序段中的移动。实施于你的应用中的 M 字母可能和这里所描述的 M 字母不同。参考你机器的程序说明书 以获得更多关于具体 M 字母应用的信息。 示例： 程序： N32 (DIS,&quot;BACK SPOT- FACING BAR D=136&quot;) N33 S115 F20 T7.7 M6 N34 G X250 Y-12 M19 N35 Z-306 N36 Y M3 N37 DWT=2 N38 G1 G29 G4 Z-300 N39 G Z-302 M5 N40 Y-12 M19 N41 ZZero axis Y在程序段 N34 中，X 和 Y 轴先定位，主轴旋转位置被控制，因此刀具可以顺利通过该孔。在下一个程序段 中，Z 轴将被指定一位置以开始加工。 在程序段 N36 中，刀具轴线被移动到与刮孔口平面中心轴一致。 刮孔口平面在程序段 N38 中被执行进行加工，完成后在接下来的程序段中，刀具重新被确定转向位置，然后 沿着 Y 轴方向移动后再回退，安全撤离该孔。45004457K244

Prima Electro S.p.A.Type of manual6.5GTS – Spindle sharingThis three-letter code enables each process to release its spindle, change its status, or acquire a new axis in a new mode. For the various spindle conditions, see the AMP manual. 语法 (GTS) (GTS, spindle_id, mode)其中： spindle_id mode (GTS)Logic identifier of the spindle axhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544is concerned. Mode requested, X = exclusive, S = shared. This is used to release a spindle. With this 语法 the process tells the system it does not want to use the spindle any longer and the spindle is made available for use by other processes. Axis status is changed to RELEASED only if the release is performed by the last owner process; if an axis is still being used by other processes, its status continues to be SHARED.(GTS, spindle_id, S) This is used to share a spindle with other processes with id spindle_id which must not be used by another process on an exclusive basis. Possible cases include: 1) A process does not own any spindle and wants to acquire a new spindle in shared mode. 2) A process owns the axis on an exclusive basis and wants to make it available for sharing. 3) A process wants to release the current spindle and acquire a new one. (GTS, spindle_id, X) This is used to use a spindle with id spindle_id on an exclusihttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ve basis. The axis will not be shared with other processes. Possible cases include: 1) A process does not own any spindle and wants to acquire one for exclusive use. 2) A process is the only owner of a shared spindle and wants exclusive control of it. 3) A process wants to release the current spindle and acquire a new one. Non envisaged cases generate a process error. Example: (GTS, 4, S) Characteristics The second field (spindle id) can be a variable; the third field (mode) can only assume the values described. Moreover, a call to the entire part program forces the block-calculation synchronism.45004457K245

Prima Electro S.p.A.Type of manual7. M 代码7.1标准 M 代码在这一章，我们简单的描述那些标准的 M 代码，这些 M 代码在下表中列出。 由于机器建立了控制器和具体应用功能之间的接口以至于你可以自定义一些符合具体应用功能的 M 代码，所 以在你的机器中使用的那些 M 代码可能和下面描述的 M 代码不相同，所以最好还是参考你机器的程序说明书 以获得更多关于每一个具体 M 代码的应用信息。M 代码 M0 M1 M2 M3 M4 M5 M6 M7 M8 M9 M10 M11 M12 M13 M14 M19 M30 M40 M41 M42 M43 M44 M45http://www.wendangwang.com/doc/efe960bed681037ac6d62544 M60 x x x x x x x x x x x x x x x x前缀激活后缀激 活 x x x取消由 周期开始 周期开始 M4-M5-M14-M19 M3-M5-M13-M19 程序停止含义可选性的程序停止 程序结束 主轴顺时针 主轴逆时针 主轴停止 刀具转换 辅助冷冻剂开启 主要冷冻剂开启 冷冻剂关闭 轴锁定 轴解锁 旋转轴锁定 主轴顺时针和冷冻剂开启 主轴逆时针和冷冻剂开启 主轴停止在指定角度 程序结束后复位至第程序开始 停用主轴范围x xM3-M4-M13-M14 M9 M9xM7-M8 M11 M11 M4-M5-M14-M19 M3-M5-M13-M19 M3-M4-M5-M13-M14x M42-M43-M44-M40 M41-M43-M44-M40 M41-M42-M44-M40 M41-M42-M43-M40 M41-M42-M43-M44 x主轴范围 1-2-3-4 范围自动改变 部件更换在 AMP 环境中，你可以指定某些 M 代码可以通过控制器复位来取消。45004457K246

Prima Electro S.p.A.Type of manual这个移动可以是点对点(G29)或者连续的(G27-G28)，其取决于 M 是如何被设置的。M 代码 M0 M1 M2 M3 M4 M5 M6 止，主轴停止和冷却液流动停止。描述 程序停止：在 M0 出现的程序段，控制器完成了该程序段的所有操作后，M0 便使程序执行停 可选性的程序停止：如果使用合适的软键命令，M1 可像 M0 编码那样使用。 程序结束：M2 定义一个程序的结束。 主轴旋转顺时针方向：M3 定义主轴顺时针旋转。其可通过从键盘键入或从程序中读取。在程序 段中，M3 在其他任何运动之前先被执行。 主轴旋转逆时针：M4 定义主轴逆时针旋转，其可通过从键盘键入或从程序中读取。在程序段 中，M4 在其他任何运动之前先被执行。 主轴停止：M5 停止主轴旋转。其可通过从键盘键入或从程序中读取。在程序段中，M5 在其他 运动之后被执行。 刀具转换：M6 先临时停止系统读取程序，然后激活 T 代http://www.wendangwang.com/doc/efe960bed681037ac6d62544码所选的刀号和刀具补偿号。在程序段 中，M6 在其他任何运动前被执行。如果它同时停止主轴旋转和冷冻剂流动，则 M6 不会禁用 M3, M4, M7, M8, M13, M14。在 M6 完成后，这些字母再次激活。M7 M8 M9辅助冷冻剂启动：M7 开启辅助冷冻剂。其可通过从键盘键入或从程序中读取。在程序段中， M7 在其他任何运动之前先被执行。 主冷冻剂启动：M8 开启主冷冻剂。其可通过从键盘键入或从程序中读取。在程序段中，M8 在 其他任何运动之前先被执行。 冷冻剂关闭：M9 关闭所有冷冻剂系统。其可通过从键盘键入或从程序中读取。在程序段中， M8 在其他任何运动之前先被执行。M 代码 M10 M11 M12 M13 M14 M19 M30 M40 M41 M42 M43 M44 M45 取消 M10 和 M12描述 线性和旋转轴锁定：M10 锁定没有参与在当前加工工序中的轴。 旋转轴锁定：M12 只锁定没有参与在当前加工工序中的旋转轴。 主轴旋转顺时针和冷冻剂启动 主轴旋转逆顺时针和冷冻剂启动 导向主轴停止：在一个程序段中，M19 主轴在该程序段中的任一动作之前已被确定方向。 M19 使 M3, M4, M13, M14 停用。 在程序结束时自动复位：M30 清除控制器缓存中的所有内容。绝对坐标原点 0 被自动启用， 所激活的当前加工程序重置到开头以于重新开始。M30 不会在主轴中取消刀具补偿。 主轴范围重设 主轴范围 1 主轴范围 2 主轴范围 3 主轴范围 4 主轴范围自动变化45004457K247

Prima Electro S.p.A.Type of manualM60工件转换45004457K248

Prima Electro S.p.A.Type of manual8. 一些变量的相关应用在一些编程应用中需要用到系统变量或者局部变量。 系统变量存储在系统的双端口内存中，且可以断电保持。 局部变量存储在内存，当系统关闭时，他们的值就会丢失。启动时，他们会调用在 AMP 中所定义的初始值。 下表列举了系统中可用的变量。 变量 E !nahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544me SN SC TIM @name 类型 局部 局部 系统 系统 系统 系统 普通变量 用户变量 系统变量 系统符号 系统时钟 (只读) PLC 变量 功能除了系统符号，所有系统和局部变量均可以被用于加工程序里面的普通数学或三角字母计算中。 一个数学计算过程是由算术操作，字母和操作数（变量或常数）组成的，如：   加 * 减 乘/ 除45004457K249

Prima Electro S.p.A.Type of manual三角字母 下表列出了系统使用的三角字母。 字母 SIN (A) COS (A) TAN (A) ARS (A) ARC (A) ART (A) SQR (A) ABS (A) INT (A) NEG (A) MOD (A,B) 描述 A 的正弦值 A 的余弦值 A 的正切值 A 的反正弦 A 的反余弦 A 的反正切 A 的平方根 A 的绝对值 A 的取整 A 的相反数 A 除以 B 的余数三角字母的运算值(SIN, COS, TAN) 必须用角度表示。反三角字母(ARS, ARC, ART)的结果同 样也必须用角度表示。布尔字母 下表列出了系统中可用的布尔字母。 字母 AND(A,B) OR(A,B) NOT(A) 描述 对两个范围在-32768  32767 的数进行位和位之间的与计算 对两个范围在-32768  32767 的数进行位和位之间的或计算 对范围在-32768  32767 的数进行位的取反布尔字母的参数必须是-32768 到  32767 范围内的整数（带符号）。只要他们在这个 范围内，他们可以是长型 E 变量。45004457K250

Prima Electro S.p.A.Type of manualGTL FUNCTIONS GTL functions available with the system are listed in the table below. FUNCTION FEL(A,B) DESCRIPTION Calculates the element having a B(1,2,3) inhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544dex from the straight line whose index is A(1=sine of the angle, 2=cosine of the angle, 3=distance from origin to the straight line). Example: E30=FEL(5,1) assigns to E30 the sine of the angle formed by the l5 straight line and the abscissa. Calculates the element having a B(1,2) index from the point whose index is A(1=point abscissa, 2=point ordinate). Example: E34=FEP(4,2) assigns to E34 the ordinate of the p4 point. Calculates the element having a B(1,2,3) index from the circle whose index is A(1=center abscissa, 2=center ordinate, 3=circle radius). Example: E42=FEC(8,3) assigns to E42 the radius of the c8 circle.FEP(A,B)FEC(A)45004457K251

Prima Electro S.p.A.Type of manual局部变量8.1E 变量E 变量的最大数量需要通过系统设置，理论上可以有多达 8000 个 E 变量。 E 变量的赋值语句形式如下： En = expression其中: n expression 示例: E37=(E31*SIN(E30) 123.4567)/SQR(16) E39=-0.00000124 5 E40=TAN(35) E31=NEG(E31) E7=81 E25=E25 30 E29=1,2,3,4,5 右边的数学计算结果存储到 E3http://www.wendangwang.com/doc/efe960bed681037ac6d625447 将此数值存储到 E39 将 35&#176;的正切值存储到 E40 将 E31 的值取相反数后存回到 E31 中 将数值 81 赋值到 E7 将 E25 的值加 30 存回到 E25 相当于 E29=1；E30=2；E31=3；E32=4；E33=5 变量序号 可以是数字，也可以是字符或者一个数学等式E 变量可以用在加工程序或者子程序里面，如果你想显示某 E 变量的当前值，可以通过使用显示命令 DIS. 例如 (DIS,E39) 可以通过手动输入指令，这个指令便会显示当前 E39 所代表的值是多少。以下这个示例表示如何赋予一个 ASCII 码字符： SCO=&quot;P&quot; E1=SC0 (DIS,E1) 其他的一些示例： XE1 X 轴当前坐标值为 E1 X-E1 X 轴当前坐标值为 E1 X(E1) X(-E1) X(E8-14*SQR(E14)) X(-(E8-14*SQR(E14))) X(E(E(E3))) FE1 SE2 TE1.E2 把 P 字符赋给字符变量 SC0 显示值为 80 (也就是 P 字母的 ASCII 码值)45004457K252

Prima Electro S.p.A.Type of manual8.2! – User variablesUser defined variables can be of two types: Long Real Character User variables must be defined in the AMP configuration. A user variable name can be up to 8 characters long. The first character must be !. The extension of a user variable may be .LR or .CH. With user variables of the character type apply this rule: !name_var[(index)].[number of characters]CH = Parahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544meter其中： indexNumber indicating the starting character in the variable character array. If index is not specified, it is taken to be zero. If specified, it must be programmed between round brackets. Specifies how many characters after the index must be read/written. 默认 值为 1. The sum of index number of characters must not be greater than the maximum number of characters configured for the specified variable. Can be: a string constant enclosed between apexes or quotes; a string variable not longer than length a numerical constant in the 0 - 255 range a numerical variable in the 0 - 255 range.number of charactersparameterExample: !ABC(1) = 125 G0 X(!ABC(1)) 125 is assigned to the !ABC(1) user variable, then this variable is used as argument of the X address in a G0 block. !CHAR(2).8CH=&quot;ABC&quot; This instruction writes &quot;ABC&quot; in the first three characters of the !CHAR user variable, starting from the second chahttp://www.wendangwang.com/doc/efe960bed681037ac6d62544racter. The remaining 5 characters (8-3) will be automatically set to zero; to prevent this, program !CHAR(2).3CH=&quot;ABC&quot; !CHAR(1).CH=&quot;A&quot; or!CHAR(1).CH=6545004457K253

Prima Electro S.p.A.Type of manualLong Real type user variables have the following format: !name_var[(index)]= Expression其中： indexexpressionNumber identifying the variable. If index is not specified, it is taken to be zero. If specified, it must be programmed between round brackets. Can be a numerical value or a mathematical expression, whose result is stored in the user variable identified by the index.Example: !ABC(1) = 125 G0 X(!ABC(1)) 125 is the value assigned to the !ABC(1) user variable; this variable is then used as an argument of address X in a G0 code. NOTES: The index of the variable can be a number or an E parameter. In motion blocks, the user variable must always be written in brackets. Examples of motion or http://www.wendangwang.com/doc/efe960bed681037ac6d62544command blocks with Long Real user variables: X(!USER1(2)) X(!USER1(2) 10) F(!USER1(1)) S(!USER1(1)) T(!USER1(1).(!USER1(2)) NOTES: The index of the variable may be a number or an E parameter.45004457K254

Prima Electro S.p.A.Type of manual系统变量 在加工程序中有四种系统变量可以使用：: 系统数字 系统字符 系统计时器 PLUS变量8.3SN – 系统数字系统数字变量是长实数型，一共有 25 个系统数字变量可以使用，在双端口内存中占据了 200 个字节。 系统数字变量的格式如下： SNn= expression其中： n expression 系统数字变量的编号，它除了可以是一个十进制数字外还可以是一个 E 变量。 表达式，它可以是数值，等式或者字符。示例： SN20 = 326.957 SN20 = (SN9*SIN(30)   12.5)/SQR(81) X(SN0) X(SN0  SN1) F(SN1) S(SN2) T(SN1).(SN3) 进给率用 SN1 的值表示 主轴转速用 SN2 的值表示 刀号用 SN1 的值表示，刀具补偿号用 SN3 的值表示 X 轴位置用 SN0 的值表示45004457K255

Prima Electro S.p.A.Type of manual8.4SC – 系统字符系统字符变量是字符类型，其被存储在系统的双端口内存中，其中有 100 字节的数列为他们保留。这意味着 所有被定义的系统字符所占容量不能超过 100 字节。 每个系统字符由一个数字指定它的地址和一个数字指定它的长度（这个长度就是表示它占用了多少个字节）v a r1 in de x v a r2 in de x 990 1 2 3 4 5 6 7 8 9 1 01 1l e n g thl e n ghttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 th系统字符变量的格式如下： SCindex.length = parameter其中： index 是指定该字符变量的地址，范围在 1 到 100 之间，这个地址编号可以用数字或者 E 变量来表示。 length 表示字符变量的长度，单个字符变量的长度最多是 80 个字符，它可以用数字表示也可以用 E 变量表 示。 parameter 赋值参数，其可以是： 字符常量，字符需要用双引号括起。 范围在0-255的数值常量 范围在0-255的数值变量，如E变量。 注意: 每个系统字符变量的地址号加上长度不能超过100。 字符变量之间可以相互赋值。 系统字符变量还可以接受与ASCII码相关的十进制赋值。 如果是数值赋值不需要双引号。 示例: SC3.5=&quot;PIPPO&quot; SC9.3=&quot;ABC&quot; or SC9.3=65,66,670 1 2 3 4 5 6 7 8 9 1 01 1 P I P P O AB C 99字符串 PIPPO 从字节 3 开始然后占据 5 个字节。 字符串 ABC 从第九个字节开始然后占据 3 个字节。45004457K256

Prima Electro S.p.A.Type of manual在定义这些字符地址和长度的时候，要注意不要和其他字符变量在位置上重叠，否则会覆盖。 示例: SC0.1=80 (DIS,SCO.1) 赋值 80 给系统字符变量。 显示 P (P 的 ASCII 码是 80)E1=80 赋值 80 到 E1 SC0.1=E1 (DIS,SC0.1) 显示 P8.5TIM – 系统计时器TIM 指令定义了控制器的时钟信息读取和显示，以秒为单位。 一个 TIM 能被读取，显示或者存储在它所支持的变量中。 示例： (DIS, TIM) E10=TIM 注意： TIM 的内容不能通过加工程序修改。8.6@ - PLUS 变量PLUS 变量即是 PLC 变量，在加工程序中是完全可以读写这个变量的。 句法 @name其中： name 是在 AMP 中为该变量所定义的名称。有三种类型的 PLUS 变量http://www.wendangwang.com/doc/efe960bed681037ac6d62544： Short Boolean Double 短型变量 布尔变量 浮点数变量Short 变量有 256 个，但是加工程序只能访问其中的 128 个。能被加工程序访问的 Short 变量的名字必须在 AMP 中有设置。它们由 16 个位组成且范围在-32768 和  32767 之间。 你同样也可以用一个 Boolean 变量访问 Short 变量的任何一个位。Boolean 变量有 256 个，但是加工程序只 能访问其中的 128 个。能被加工程序存取的 Boolean 变量的名字必须在 AMP 中有设置。 Double 变量有 64 个，都能被加工程序所访问，能被加工程序存取的 Double 变量的名称必须在 AMP 中有设 置。45004457K257

Prima Electro S.p.A.Type of manual全部 Boolean, Short 和 Double 变量的数量也要在 AMP 中有设置。 当系统启动时，所有在 AMP 中设置的 PLUS 变量的值会被加载。如果一个变量的 value 处为空，系统会将其 忽略。 PLUS 变量可以被用在如下的加工程序中： 1. 在赋值语句和三字码指令中 E10=@LOG1 (GTO,END,@LOG3=1) 2. 运动程序段 G0 X (@LOG2) X(@LOG2 2) F(@LOG2) S(@LOG3) T(@LOG2) (@LOG3) 由于这些变量和机器逻辑直接相连，机床制造商必须向你提供这些变量被定义后的使用目的和设 置说明。8.7L 变量L 变量是长实数型变量，15 位带符号数和至多 12 位整数。有 400 个 L 变量，地址号从 0 到 399。 这些变量和用户表格，PLUS 里面的的变量是一一对应的，可以应用在加工程序里面和逻辑 PLC 里面。 示例： L10 = 26.9570 L15 = (L10*SIN (30) 9)/SQR(81) (GTO,END,L2=1) G0XL15 X(L15) X(L15 L1) FL1 SL1 TL1.L3 由于这些变量和机器逻辑 PLC 直接相关，机床制造商必须向你提供应用中使用的变量表http://www.wendangwang.com/doc/efe960bed681037ac6d62544及正确处 理这些应用所需要设置信息。45004457K258

Prima Electro S.p.A.Type of manual8.8Multiple AssignementsWith the multiple assignment operators   it is possible to assign the contents of other variables to a certain number of variables. Multiple assignment is accepted only for numeric variables. 语法 destination_variable =  source_variable, number_variables  其中： destination_variable source_variable number_variables Examples: E0 =  SNO,4  is equivalent to the following four assignments: E0 E1 E2 E3 = = = = SN0 SN1 SN2 SN3Is the first destination variable. Is the first of the source variables. Is the number of variables to transfer. This can be an integer or a local or system variable.E100 = 5 E50 =  LO,E100  is equivalent to the following five assignments: E50 E51 E52 E53 E54 = = = = = L0 L1 L2 L3 L445004457K259

Prima Electro S.p.A.Type of manual9. 固定循环9.1 9.2 9.3 固定循环 G8n代码 G81 至 G89 定义固定循http://www.wendangwang.com/doc/efe960bed681037ac6d62544环，其可以让你对多种加工操作进行编程，对于多个相同的加工操作不需要进行 重复地编程。 在程序段中编写 G81-G89 固定循环时，不能编程轴的运动指令。因为固定循环指令只是写入加工模式而不是 执行运动指令，固定循环的执行从含有 G81-G89 的程序段开始。 固定循环的主轴可以在 G81-G89 程序段中指定。 例如，在 G81 R Y-20 程序段中，Y 轴是该固定循环的主轴。 G8n 功能字母。在编程一个新的固定循环之前，必须首先用 G80 取消目前的固定循环。G80 字母必须在位于 上一个固定循环后的程序段中编程。 当切割直径补偿(G41/G42)处于活动状态时，不能编程 G8n 程序段。 当一个固定循环，例如 G82, G83, G89 要求一个停留时间，你可以： 使用在AMP中定义的默认停留时间 编程一个包含变量DWT=time的程序段（以秒为单位）IMPORTANT固定循环同样也可以在虚拟轴上执行。固定循环特点 该表列出了 10 系列中可以使用的固定循环和他们的特点。 固定循环 G81 G82 G83 G84 G85 G86 G89 G80 钻孔 锪孔 深孔钻孔 攻丝循环 铰孔循环 镗孔循环 镗孔循环 带鍃加工 取消固定 循环 钻孔开始进给 切削进给 切削进给 间歇进给 切削进给 切削进给 切削进给 切削进给 延时 否 是 否 否 否 否 是 旋转 普通 普通 普通 逆转 普通 停止 普通 快速返回 快速返回 快速返回 切削进给到 R1 位置 快速退回到 R2 位置 切削进给到 R1 位置 快速退回到 R2 位置 快速返回 切削进给到 R1 位置 快速退回到 R2 位置 返回45004457K260

Prima Electro S.p.A.Type of manual固定循环的运动 当系统读取到程序中的固定循环时，执行的动作顺序如下： 1. 快速定位于孔的中线 2. 快速靠近到工作平面（R1指定的位置） 3. 加工进给到Z所指定的深度 4. 循环作用于孔的底部 5. 快速或加工进给速率回到R位置（如果R2的位置和R1不同则是在R2位置）Feed motion1Rapid2 R1http://www.wendangwang.com/doc/efe960bed681037ac6d625443 5Z 4…………快速进给率 -------------加工进给率固定循环的一些示例. 两种典型的固定循环载于本节。 下面是一个固定循环，其靠近坐标 R1 和返回坐标 R2 相同。Feed motionG81 R1 . . Z. . R1 = 靠近加工平面的位置 Z = 孔的深度RapidR1Z45004457K261

Prima Electro S.p.A.Type of manual以下的这个示例则是返回位置不同于靠近加工平面位置。Feed motionG81 R1. . R2. . Z. .RapidR1 = 靠近加工平面的位置R2R2 = 返回的位置 Z = 孔的深度R1Z45004457K262

Prima Electro S.p.A.Type of manual9.4句法G81- 钻孔循环G81[G-codes] R1.. [R2..] Z.. [F.. ] [auxiliary]其中： G-codes 其他与 G81 兼容的 G 代码（见第一章的”兼容的 G 代码”表）。R2R1靠近加工平面的位置（必须的）。其定义当循环开始时，快速定位到加工平面的位置坐标。R 地址后接位置值，其可以直接 间接用一个 E 变量表示。用数字或R1FR2 示。 Z其定 义在 加工 后返 回的 坐 标。 R 地 址后 接返 回值 。 如果 其被 省 略，控制器默认是 R1。R2 可以直接用数字或间接用一个 E 变量 表Z其定义孔的底部坐标（特别是 Z）。Z 地址后接深度坐标值，其 可以直接用数字或间接用一个 E 变量表示。 F 其定义固定循环操作中的进给速率。其用 F 指令编程，后接进给率数值。 T 指令。在一个固定循环程序段中，可以至多auxiliary M, S 或 编程 4 个 M 代码，1 个 S（主轴速度）和 1 个 T（刀具选择）示例：45004457K263

Prima Electro S.p.A.Typhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e of manual0.Z 意为 Z=0 程序： (UGS,X,0,110,Y,0,80) N31 (DIS,&quot;TWIST DRILL D=6.5&quot;) N32 S1100 T3.03 M6 N33 G81 R3 Z-15 F95 M3 1 2 3 4 N34 X15 Y15 N35 Y60 N36 X80 N37 Y15 N38 G80 Z50 M5 N39 M30 G81 指明了钻孔加工 在（15, 15）处钻孔 在（15, 60）处钻孔 在（80, 60）处钻孔 用 G80 取消 G81 定义加工的 X 和 Y 的范围：0&lt;X&lt;110; 0&lt;Y&lt;80 显示信息“TWIST DRILL D=6.5”9.5句法G82 -锪孔循环G82[G-codes] R1.. [R2..] Z.. [F.. ] [auxiliary]其中：R2 R1FZG-codes R1 R2 Z F auxiliary其他与 G81 兼容的 G 代码（见第一章的”兼容的 G 代码”表）。 定义孔起点值（见 G81） 定义返回坐标（见 G81） 定义孔终点值（见 G81） 定义进给速率（见 G81） M, S 或 T 指令。45004457K264

Prima Electro S.p.A.Type of manual示例： 下图是一个锪循环。G82 R5 Z-15 F.. M.. X.. Y..9.6 9.7 9.8 9.9 9.109.11句法G83- 深度钻孔循环G83 [G-codes] R1.. [R2..] Z.. I.. [J..] [K..] [F.. ] [auxiliary]其中： G-codes 其他与 G81 兼容的 G 代码（见第一章的”兼容的 G 代 码” R1 R2 Z 表）。 定义孔起点值（见 G81） 定义返回坐标（见 G81） 定义孔终点值（见 G81）I 定义每次啄钻拉出后进入下一个啄钻时的深度增量。I 后接 深度增加值。 J 定义最低限度深度增量，在增量值逐级递减以致小于这个值 时，便会以此http://www.wendangwang.com/doc/efe960bed681037ac6d62544为增量值，而且接着后面的啄钻都会恒定采用这个增量值直至加工完成， J 后接最小深度增量 值。 K 啄钻深度增量值递减系数，也就是用在 I 值，每次啄钻循环完成后下一个深度增量值就是上一个的增量值 会乘以这个系数得出。这样进行递减直到增量值小于 J 所指定的数值。K 地址后接一个数值。 F 定义进给速率（见 G81） M, S 或 T 代码。auxiliary45004457K265

Prima Electro S.p.A.Type of manual说明： 用 G83，不同的运动情况都可能发生。 如果 I, J 和 K 有编程，轴移动如下： 1. 快速靠近孔中心线 2. 快速靠近R坐标 3. 以加工进给速率移动到R   I坐标位置 4. 每次碎片流出发生时，每次快速退回至最开始的那个R坐标位置以带出加工产生的碎屑。 5. 用下面的公式计算新的R值： 6. R = Rold   I - X (其中 X 默认是1, 或者, 如果 DRP 变量有定义,就会是DRP的值) 7. 用下面的公式计算新的I值： I = Iold * K 如果 I * K &gt; J I = J 如果I * K &lt; J 8. 重复2至6，直至达到Z指定的位置。 断屑循环 如果 J 和 K 参数没有被设定，下面的动作会产生： 1. 快速靠近孔中心线 2. 快速靠近R位置坐标 3. 以加工速率到R   I位置 4. 主轴按DWT定义的时间停留，或按标准时间停留，如果DWT没有编程。 5. 重复3和4，直至达到Z位置。示例：45004457K266

Prima Electro S.p.A.Type of manual注释：0.Z 意为 Z=0 程序： N65 (DIS,&quot;TWIST DRILL D=6&quot;) N66 S930 F65 T6.6 M6 N67 G83 R8 Z-55 I20 K.8 J6 M13 N68 X-15.81 Y-22.2 N69 X23 N70 X9 Y35.8 N71 G80 Z50 M5 N72 M30 深度的增量值变化就是等比为 K=0.8 的http://www.wendangwang.com/doc/efe960bed681037ac6d62544等比数列 初始增量值是 I=201 2 39.12DRP – G83 下一啄钻循环开始的准备距离DRP 命令定义 G83 循环中的下一啄钻循环开始的准备距离，以 mm 为单位。 这个值可以由系统初始化为 1. 其可以从键盘或加工程序中赋值。 句法 DRP=value其中： value 可以直接或间接用一个 E 变量编程。 示例： DRP=0.01 DRP=5复位后会恢复 1 为默认值。45004457K267

Prima Electro S.p.A.Type of manual9.13G84 – 无编码器的攻丝循环该 G84 代码在没有安装编码器的主轴上运作。 句法 G84 [G-codes] R1.. [R2..] Z.. [F.. ]R2 K R1Fz其中： G-codes R1 R2 Z F 其他与 G81 兼容的 G 代码（见第一章的”兼容的 G 代码”表）。 定义快速靠近坐标。 定义快速返回坐标。 其定义孔的深度（特别是 Z）。Z 地址后接深度坐标，其可以直接用数值或间接用一个 E 变量编程。 其定义固定循环操作中的进料速率。其用 F 地址编程，后接进料速率值。说明： 刀具快速靠近工件时必须在到攻丝螺距 5 倍的距离前停止。。 攻丝进给率必须用下面的公式计算： F = S * p * 0.9 其中： S p 0.9 主轴旋转速度 螺距 保持刀架弹簧补偿器张开的进给率减少因数最后的 Z 必须比实际拍打工作行程减少 10%。 最后的 Z 必须足够长以让轴达到编程的进给率，并以控制的减速停止。其必须根据主轴旋转停止所需的时间 来计算。如果最后的 Z 不够长，控制器会显示错误。45004457K268

Prima Electro S.p.A.Type of manualM 代码在 G84 程序段中不允许。45004457K269

Prima Electro S.p.A.Type of manual示例：A-A Section注释： 0.Z 意为 Z=0 程序： (UGS,http://www.wendangwang.com/doc/efe960bed681037ac6d62544X,-60,60,Y,-70,70) N90 (DIS,&quot;TAP M8-TRACTION TYPE COMPENSATOR&quot;) N91 S280 F315 T8.8 M6 M13 N92 G84 R7 Z-15 N93 X-51.96 Y-30 N94 X51.96 N95 X Y60 N96 G80 Z50 M5 这个程序对 R.H.攻丝操作有效，因为 M13 在程序段 N91 中被编程。对于 L.H.攻丝操作，只要编程 M14（或 M04）而不是 M13（或 M03）。45004457K270

Prima Electro S.p.A.Type of manual9.14G84 –带编码器的攻丝循环G84 在安装了编码器在主轴上的系统的运作。 句法 G84 [G-codes] R1.. [R2..] Z.. [K..] [F.. ] [auxiliary]其中： G-codes 同 G81 兼容的其他 G 编码（见第一章“兼容的 G 编码”表）。R1 靠近坐标（必须的）。定义在加工平面的快速定位坐标，当循环开始时。快速靠近值跟在 R 地址后。其 可 R1 R2 K F 以直接用一个十进制数编程或用一个 E 参数间接编程。 定义快速靠近坐标。 定义快速返回坐标。 定义螺距。K 后跟一个值。 定义用在固定循环操作中的进给率。其用 F 编程，进给率值跟在 F 之后。 M, S 或 T 码（见 G81）。auxiliary 说明：编码器安装在主轴上后，G84 编码可以按如下被编程： 通过计算 F 进给率，好像在编码器上没有主轴一样。 通过使用 K 线距。在这种情况下，控制器通过主轴速度和 K 相乘自动计算进给率，以 rpm 为单位。在攻丝循环中，控制器忽略 CYCLE STOP 按钮（除了在快速横贯靠近部分）和 FEEDRATE OVERRIDE 选择器（软键）。 SPINDLE SPEED OVERRIDE 选择器必须由机器逻辑禁用。要中止攻丝循环，&quot;INTP-ABO&quot;逻辑字母 可被使用（在 Plus 变量手册中见变量描述）。 示例： N90 (DIS,http://www.wendangwang.com/doc/efe960bed681037ac6d62544&quot;TAP M8&quot;) N91 S280 T8.8 M6 M3 N92 G84 R7 Z-15 K1 N93 X-51.96 Y-30 N94 X51.96 N95 X Y60 N96 G80 Z50 M545004457K271

Prima Electro S.p.A.Type of manual9.15TRP(RMS) – Tapping Return PercentageThe TRP command defines the feedrate percentage variation applied in the retract phase of the tapping cycle. This command is normally defined in a program, but can also be used in blocks entered with a keyboard command or by means of a softkey. 语法 TRP = value其中： value can be programmed directly with an integer number or indirectly with an E parameter of the byte type. Example: TRP = 110 TRP = 10represents  10% of the programmed F represents - 90% of the programmed F9.16句法G85 – 绞孔循环G85 [G-codes] R1.. [R2..] Z.. [F.. ] [auxiliary]其中： G-codes 码”表） R1 R2 Z F 编程。 auxiliary M, S 或 T 码（见 G81）. 定义快速靠近坐标和到工作的固定返回。 定义快速返回坐标。 定义孔深（通常是 Z）。Z 地址后跟深度坐标，该值可以直接 定义用于固定循环操作的进给率。其用 F 后跟随的进给率值 与 G81 兼容的其他 G 编码（见第一章的“兼容 Ghttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 编用一个十进制数编程或用一个 E 参数间接编程。45004457K272

Prima Electro S.p.A.Type of manual9.17句法G86 -镗孔循环G86 [G-codes] R1.. [R2..] Z.. [F.. ] [auxiliary ]其中： G-codes 与 G81 兼容的其他 G 编码（见第一章的“兼容 G 编码”R2 R1表）。 R1 定义快速靠近坐标和到工作的固定返回。 定义快速返回坐标。FR2zZ 定义孔底坐标（通常是 Z）。Z 地址后跟底部坐标值，该值可 以直接用一个十进制数编程或用一个 E 参数间接编程。 F 定义用于固定循环操作的进给率。F 后跟随的进给率值编程。 auxiliary M, S 或 T 码（见 G81）.9.18句法G89 –带鍃孔的镗孔循环G89 [G-codes] R1.. [R2..] Z.. [F.. ] [auxiliary ]其中： G-codesR2 R1与 G89 兼容的其他 G 编码（见第一章的“兼容 定义快速靠近坐标和到工作的固定返回。 定义快速返回坐标。 定义孔深（通常是 Z）。Z 地址后跟深度坐标，该值可 定义用于固定循环操作的进给率。其用 F 地址后跟随的 auxiliary M, S 或TG 编码”表）。 R1 R2 ZFz以直接用一个十进制数编程或用一个 E 参数间接编程。 F 进给率值编程。可编程辅助字母。在一个固定循环程序段中，你可以编程至多 4 个 M 字母，1 个 S（主轴速度）和 1 个 T（刀具选择）。45004457K273

Prima Electro S.p.A.Type of manual45004457K274

Prima Electro S.p.A.Type of manual在一个固定循环中使用 2 个 R 范围 你可以编程 2 个 R 在一个固定循环中，当孔必须被钻，攻丝，绞等时，在同一平面，但是被阻碍分隔开（夹 子，在重复子平面的孔http://www.wendangwang.com/doc/efe960bed681037ac6d62544，等等）。 示例： 注释： 0.Z 意为 Z=0 程序： N41 (UGS,X,0,100,Y,0,150) N42 (DIS,&quot;TWIST DRILL D=10&quot;) N43 S850 F100 T4.4 M6 N44 G81 R-10 R2 Z-36 M3 N45 X35 Y40 N46 X65 Y80 N47 X35 Y120 N48 G80 Z50 M5更新固定循环范围 当一个固定循环在一个程序中激活时，你可以编程带快速靠近，返回和深度坐标的程序段，以更新循环动作 而不用重新编程这个循环。 编程格式为 X, Y, R1, R2, Z 的程序段，其按下面的顺序执行： 1. X和Y 2. 更新R1 – 新的快速靠近坐标 3. 更新Z – 新的深度 4. 更新R2 – 新的返回坐标 下面总结了用于更新固定循环的程序程序段格式： 格式 X.. Y.. Z.. X.. Y.. R.. X.. Y.. R.. R.. X.. Y.. R.. Z.. X.. Y.. R.. R.. Z.. R.. R.. R.. R.. Z.. R.. R.. Z.. 动作 用一个新的 Z 深度在 XY 执行一个固定循环 用新的 R1 快速平面在 XY 执行一个固定循环 用新的(R1)快速平面和(R2)返回范围在 XY 执行一个固定循环 用新的 R1 快速平面和 Z 深度在 XY 执行一个固定循环 用新的 R1 快速平面，R2 返回范围，和新的 Z 深度在 XY 执行一个固定循环 更新 R1 快速平面，且在当前位置不执行固定循环 更新 R1 快速平面和 R2 返回范围；在当前位置不执行固定循环 更新 R1 快速平面和 Z 深度；在当前位置不执行固定循环 更新 R1 快递平面，R2 返回，和 Z 深度范围；在当前位置不执行固定循环45004457K275

Prima Electro S.p.A.Type of manual在执行中更新 R 范围（上限和下限） 例 1： 注释： 0.Z 意为 Z=0 程序： N35 (DIS,&quot;TWIST DRILL D=8&quot;) N36 S1000 F100 T4.4http://www.wendangwang.com/doc/efe960bed681037ac6d62544 M6 N37 G81 R3 Z-42 M3 1 N38 X15 Y15 2 N39 X65 3 N40 Y85 R-13 4 N41 X15 N42 G80 Z50 M5例 2：20注释： 0.Z 意为 Z=0 程序： (UGS,X,0,100,Y,0,200) N42 (DIS,&quot;TWIST DRILL D=8&quot;) N43 S1000 F100 T5.5 M6 N44 G81 R-18 Z-46 M13 1 N45 X25 Y25 2 N46 X75 R-18 R-8 3 N47 Y75 R-8 R2 Z-25 4 N48 Y175 R-3 Z-46 5 N49 X110 N50 G80 Z50 M545004457K276

Prima Electro S.p.A.Type of manual例 3：A-A Section注释： 0.Z 意为 Z=0 程序： (UGS,X,0,100,Y,0,200) N42 (DIS,&quot;TWIST DRILL D=8&quot;) N43 S1000 F100 T4.4 M6 N44 G81 R-18 Z-42 M3 M8 N45 X25 Y25 N46 X75 R-18 R4 N47 Y125 R-14 R4 N48 Y225 R-18 N49 X110 N50 G80 Z2 M51 2 3 4 5 645004457K277

Prima Electro S.p.A.Type of manual10. PARAMACROStill to be translated45004457K278

Prima Electro S.p.A.Type of manual11. 测量循环11.1 电子探头电子探头是一个安装在主轴上并像刀具一样受控的测量工具，探针也有长度和直径补偿，除了这些，它也可 以安装在固定的位置上作为一个电子感应器来测量刀具长度，下图表示一个电子探头和它相关的模型。SpindleProbedL电子探头 Probhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e 探头，Spindle 主轴 当电子探头安装在主轴上时一些 G 代码表现出专门的测量循环或者探针循环。 G 代码 G72 G73 G74 测量一个点的坐标 测量一个圆的中心和半径 测量与参考点位置的差值（探头是安装在固定的位置而不是在主轴上） 功能系统会将测量数据存入到事先在测量循环（G72-G74）定义好的 E 变量当中去。当系统执行一个测量循环， 执行顺序如下： 1. 快速到达临近点（Pa） 2. 以测量的速度移动到探针触动开关位置，然后停止保存测量数据。如果探针触动开关一直未被触发， 则最远也不会超过安全行程点（Ps） 3. 快速返回到测量循环起点（如果是G73的话就停在孔的中心）。45004457K279

Prima Electro S.p.A.Type of manual下图描述了测量循环的运动过程。Theoretical dimensionFeedPa RAPIDPsVmQa Cycle start positionQsAxis movementCycle start position 量刀起点 Axis movement 轴的运动方向 Rapid 快速 Feed 进给率 测量循环中以下的错误可能发生： 如果探头在到达安全极限点之前仍未触发感应开关，那么探头将会退回到起点位置，然后系统会显示 一条信息且系统处于错误状态。 如果探头在成功完成测量后返回不到起点，系统会显示一条信息且系统处于错误状态。 如果测量是发生在快速移动到靠近点之前，探头会退回到起点，然后系统会显示一条信息且系统处于 错误状态。 NOTE: If the probing cycle is executed with G27 or G28 active, both the approaching movement and probing are carried out in continuous mode, while the stopping movement obtained after the probe input has been found is executed in point tohttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 point mode.所获得的测量数值单位是 AMP 里面所定义的，也就是说受 G70/G71 的影响。测量循环预设 当你第一次用到测量循环，也或者是任何量刀的条件有所改变时，你都必须： 1. 定义测量循环的参数 2. 测量探头的直径。 3. 使探头和主轴所在运动轴相关联。 4. 测量探头的长度值。45004457K280

Prima Electro S.p.A.Type of manual11.2DPP (DPT) – 定义测量循环参数可以通过键盘或者一个程序来输入 DPP 命令来定义测量循环的参数。如果没有指定这些参数的话那么系统会 去读取 AMP 里面的预设值。 句法 (DPP,approach,safety,speed[ , mode ] )其中： approach 是量刀靠近到预计位置之前的缓冲距离，例如目标位置估计在 100，而这里设为 10，则探头 会在 100-10=90 处位置由快速移动转为所设的进给率移动来靠近目标。 safety 安全容许值，定义探测位置最远不能超出所预计的位置加上此值，例如预计位置在 100，则探头移动 最远是 100 12=112，到达 112 仍未触发开关则会停止并报警。 speed 测量时候的进给率 mode 用来指明测量完成后是否快速退回到起点位置，它可以设为以下的数值： 0 = 实行快速退回 1 = 不执行快速退回 默认值是 0 示例: (DPP,10,12,1000) 测量球形探头直径方向补偿 去测量球形探头的直径补偿，是为了补偿由于测量过程中探头接触到物体后到探头开关触发时之间的行程。 为此你需要准备一个标准的，已知尺寸的圆环，圆筒或者相似的物体，该物体的中心是工件原点 9 的 X 和 Y 零点。 探头校正 经常地，在用一个探头之前，由于安装的原因，球形探头的中点没有和主轴所在的轴方向一致，所以此时球 形探头的中心与其有偏差，偏差值通过校验的方法测定得出，此时你需要准备一个标准的，已知尺寸的圆 环，圆筒或者类似的物体，这个物体的中心是工件原点 9 的 X 和 Y 的零点。 垂直方向上校验探头并测定补偿值 为了测量探头在垂直方向上因为接触到物体http://www.wendangwang.com/doc/efe960bed681037ac6d62544到触发的行程引起的误差，你需要校验，此时此时你需要准备一 个标准的，已知尺寸的圆环，圆筒或者类似的物体，这个物体的顶部或者是上表面是工件原点 9 的 Z 的零 点。45004457K281

Prima Electro S.p.A.Type of manual示例: N1 (DIS, &quot;DPP, UPA, UPO, &quot;) N2 T30.30 M6 N3 (UAO, 9) N4 (DPP, 10, 12, 600) N5 UPA=0 N6 UPO=0 N7 E30=... N8 E31=E30/2 N9 E32=... N10 E33=E31 10 N11 GB0 N12 XY N13 Z-4 N14 G73 rE31 E40 - 指定从 Z=0 到校验用的圆环的上表面的距离，通常都是 0。 - 把校验用的圆环的直径赋值到该变量 -探头装在主轴上 - 设定探测参数 - UAO 与 UPO 在后面有介绍，这里先清零。- 用 G73（后面有介绍）测量孔的坐标（圆心和半径）N15 Z100 N16 (DIS, &quot;UPA=&quot;, E40, &quot;UPO=&quot;, E41) N17 M0 N18 UPA=E40 N19 UPO=E41 - E40 是校正出来的圆心的 X 的偏差值 - E41 是校正出来的圆心的 X 的偏差值N20 E34=(E30-E42*2) - 直径方向的补偿值 N21 (DIS, &quot;DIAMETER=&quot;, E34) N22 M0 N23 (RQP, 30, 30, dE34) N24 T30.30 M6 N25 GXYE33 N26 G72 ZE32 E43 N27 N28 N29 N30 N31 N32 - 保存该补偿值 - 启用新的补偿值 - 用 G72（后面有介绍）来测量圆环上表面的位置来校正探头 Z 方向。E35=E43-E32 - 测定理论与实际的 Z 方向的偏差值，作为补偿值 Z100 (DIS &quot;VARIANCE.Z=&quot;, E35) M0 (RQP, 30, 30, LE35) M30http://www.wendangwang.com/doc/efe960bed681037ac6d6254445004457K282

Prima Electro S.p.A.Type of manual测量循环 以下是测量循环的 G 代码： G72 G73 G74 点的测量（带球形探头的直接补偿） 孔的参数测量 点的测量（不带球形探头的直径补偿）在 G72，G73 和 G74 中，E 变量并不是以程序中的轴排序编号来依次存储结果，而是以 AMP 中的顺序为准， 如: AMP 中轴定义的顺序为：XYZ G72 X100 Y50 E32 G72 Y50 X100 E32 以上两种情况都是 E32 存储 X 而 E33 存储 Y。 在 UPR 所定义的虚拟坐标系中，补偿值是以虚拟坐标系为参考的。11.3G72 - 点的探测G72 可以使你用一个线性移动来让探头去探测一个点的坐标值。 句法 G72 axis1 [ axis2] [axis3] E-par其中： axis1 . . . axis3 是参与这个循环中的轴名称，这里编程的轴坐标是 目标理论位置，也就是探头要碰到的点的估算位 置，在 G72 中你可以最多编程三个轴。 E-par 定义 E（x）变量来存储第一轴的测量结果，该 E 变 量的后面的 E（x 1）和 E（x 2）依次存储第二第 三轴的结果。 说明： The co-ordinates measured by the probe are stored in E parameters that are defined by the G72 cycle. The control stores the co-ordinates of the axes beginning with the E parameter specified in the cycle. Measures are taken applying cutter diameter compensation to the probe. To ensure high accuracy the surface must be perpendicular to the measuring move. The probe can also be perhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544formed on virtual axes activated by the UPR function or on the axis which identifies the direction of the activated tool (TCP, 5). When the probe is performed on the virtual axes defined with UPR, the values measured in relation to the virtual axes are stored in E (x), E (x 1), E (x 2). When the probe is performed on the tool directional axes, the system stores the value of dimensions measured in relation to those axes in E (x) and the values measured, in relation to the part of the Cartesian linear axes defined in the TCP table or corresponding virtual axes if UPR virtual mode is active45004457K283

Prima Electro S.p.A.Type of manualin E (x 1), E (x 2), E (x 3). 示例： AMP 中轴定义的顺序为：XYZ G72 X100 Y50 E32 G72 Y50 X100 E32 以上两种情况都是 E32 存储 X 而 E33 存储 Y。 示例： 在虚拟坐标系里面使用的情况。 (UPR,0,XYZ,UWV,30,25,0) G72 U25 V-10 W-25 E30 UVW 三个虚拟轴坐标值会依次存入到 E30，E31，E32 当中。11.4G73 – 孔探测循环G73 能让你用一个探头去测量当前插补平面内的一个孔的尺寸。 句法 G73 r.. E-parhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544其中： r 定义孔的理论半径。 E-par 系统开始存储测量数据的首个 E 变量 地址： 第一个 E 变量是存储圆心横坐标，通常是 X。 第二个 E 变量是存储圆心横坐标，通常是 Y。 第三个 E 变量是存储半径特征: 这个测量方式也可以运用在由 UPR 所激活的虚拟轴坐标上面。 在启用 G73 循环之前，刀具所在轴必须定位到圆心位置，测量过程中还采取了探头的直径补偿。45004457K284

Prima Electro S.p.A.Type of manual探头的移动顺序 示例： G73 r100 E55 这个孔的圆心横坐标，纵坐标和实际的半径分别存入 E55，E56，E57。11.5G74 -刀具规格循环G74 是一个刀具规格循环。G74 采用一个固定位置的探测器来测量刀具规格。 句法 G74 axis1 [ axis2] [axis3] E-par其中： axis1. . . axis3 最多可以三个轴。 E-par Defines the E(x) parameter for storing the deviation from the point measured and the point programmed for the first axis programmed in G74. The deviation values of the other axes, if programmed, are stored sequentially in E(x 1) and E(x 2). 说明： G74 用于测量一个刀具的规格或者检测刀具的磨损。 The steps in the G74 cycle are similar to those in the G72 cycle. The difference between both cycles is how the control executes calculations based on measured dimensions. The control does not consider the diameter of the phttp://www.wendangwang.com/doc/efe960bed681037ac6d62544robe ball and stores the variance from theoretical dimensions in the parameters specified in the G74 block. The probe can also be performed on virtual axes activated by the UPR function or on the axis which identifies the direction of the activated tool (TCP, 5). When the probe is performed on the virtual axes defined with UPR, the deviation values between the points measured and the programmed points in relation to the virtual axes are stored in E (x), E (x 1) and E (x 2).45004457K285

Prima Electro S.p.A.Type of manualWhen the probe is performed on the tool directional axes, the system stores the deviation value between the point measured and the programmed point in relation to that axis in E (x) and the values measured, in relation to the part of the Cartesian linear axes defined in the TCP table or corresponding virtual axes if the UPR virtual mode is active in E (x 1), E (x 2) and E (x 3) . Example: G74 X60http://www.wendangwang.com/doc/efe960bed681037ac6d62544 E41 E41 is given by the formula: E41 = Pm - Pt其中：Pmis the measured point Pt is the theoretical point11.6UPA (RTA) - Update Probe AbscissaDefines the probe requalification value for the abscissa (typically X). 语法 UPA=value 其中： value is the abscissa requalification value expressed in millimetres.11.7UPO (RTO) - Update Probe OrdinateDefines the probe requalification value for the ordinate (typically Y). 语法 UPO=value 其中： value is the ordinate requalification value expressed in millimetres.11.8ERR - Managing Probing ErrorsCycles G72, G73 and G74 enable you to handle process errors either automatically or from part program. You can choose the method by setting the ERR parameter. For further information on probing error management see Appendix C45004457K286

Prima Electro S.p.A.Type of manual关于非固定位置的探头的操作 对于 G72 和 G73 的测量循环你可以： 用以下方式校正工作原点：     测量有参照意义的物体表面 置于一个已知规格的孔中测量以下尺寸数据：     直径 平面和孔深http://www.wendangwang.com/doc/efe960bed681037ac6d62544测量一个表面来校正工作原点 工作原点的改变可以因为： 温度变化（温度产生的漂移） 新的加工托盘 这些的改变都需要你通过探测一个已知表面来校正工件原点 温度漂移 下面是通过一个摆在准确位置的测试方块来校正工作原点的步骤：Cubic gauge45004457KReal distanceE33287

Prima Electro S.p.A.Type of manual主程序： . . . N99 E33=-300 . . . /N100 (CLS,TEST3) 子程序 TEST3: N500 (DIS,&quot;RQO-DT&quot;) N501 G72 Y(E33) E32 N502 E32=E32-E33 N503 (RQO,1,Y(E32)) N504 (RQO,2,Y(E32)) N505 (RQO,3,Y(E32)) 新的加工托盘 ;测得的位置存放在 E32 ;校正工作原点 1 的 Y 位置 ;校正工作原点 2 的 Y 位置 ;校正工作原点 3 的 Y 位置02主程序： M...; N199 T30.30M6; N200 (UAO,2) N201 GXY N202 E10=2 N203 E34=-250 /N204 (CLS,TEST4) TEST4 子程序： N500 G72 Y(E34) E30 N501 E31=E30-E34 N502 (RQO,E10,Y(E31)) ;校正工作原点 2 的 Y 位置 ;托盘更换 ;装载探头到主轴45004457K288

Prima Electro S.p.A.Type of manual通过一个已知尺寸的孔来校正工作原点 在你应用该校正方式时，你必须编写合适的 X 和 Y 位置让探头移动到孔中 示例： N200 (DIS,&quot;REQUALIFYING ORIGIN FOR X AND Y AXES&quot;) N201 T11.11 M6 N202 GX180 Y60 N203 Z-130 N204 G73 r50 E35 ;Measuring cycle diameter 100. X anhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544d Y coordinates are N205 E35=E35-180 ;stored in parameters E35 and E36 N206 E36=E36-60 N207 (RQO,1,X(E35),Y(E36)) ;Requalifies origin 1 for X (E35) and Y (E36) Checking Diameters You can use a probe to check the hole diameters. With proper programming you can compare detected values with allowed values, and decide whether to continue machining or branch to a block containing a label. In the following program, the control measures the deviation between the actual and the theoretical diameter of a hole and compares this deviation with the tolerances. The comparison may have three different results and courses of actions: Hole diameter is within the allowed tolerance - the program continues. Hole diameter is greater than the allowed tolerances - tool is automatically timed out of use (label A3). The program stops (M00) and the part is rejected. Hole diameter is less than the allowed tolerances - tool is automatically timed out of use http://www.wendangwang.com/doc/efe960bed681037ac6d62544(label A4). The program branches to label A1, where the hole reaming cycle is repeated using the alternative tool that is specified in the tool life file. Example: The following is an example of diameter checking. Hole diameter and tolerance: D=100  0.02/-0.01545004457K289

Prima Electro S.p.A.Type of manualProgram: &quot;A1&quot; N111 N112 GZ-150 N113 (DIS,&quot;REAMING HOLE D=100&quot;) N114 F..S..T13.13 M6 N115 GX-120 Y80 M13 . . . N129 (DIS,&quot;HOLE TOLERANCE CHECK D=100&quot;) N130 T14.14 M6 N131 GX-120 Y80 N132 Z-85 N133 G73 r50 E30 N134 E32=E32*2 N135 (DIS,E32) N136 (GTO,A3,E32&gt;100.02) N137 (GTO,A4,E32&lt;99.985) N138 GZ150 N139 (DIS,&quot;WORKPIECE IN TOLERANCE&quot;) . . . N2100 M30 &quot;A3&quot; N2101 (DIS, &quot;Hole too big&quot;) N2102 M00 &quot;A4&quot; N2103 (DIS, &quot;Hole too small&quot;) /N2104 (GTO,A1);probe in spindle ;XY positioning to hole center ;Z positioning ;hole radius stored http://www.wendangwang.com/doc/efe960bed681037ac6d62544in E3245004457K290

Prima Electro S.p.A.Type of manualChecking Plane Dimensions and Hole Depths You can use a probe to check the dimensions of planes and the depths of holes. With proper programming you can compare detected values with allowed values, and decide whether to continue machining or branch to a block containing a label. In the following programming example, the control detects the deviation of actual dimensions from programmed dimensions. It compares this deviation with allowed tolerances. The comparison has three possible results: Continue machining Stop machining and reject the part because the dimension is too long Requalify the tool and repeat the program from label C1 because the dimension is too short Example: The following example check of the dimensions of a plane Theoretical dimension, with respect to Z axis zero: - 80 &#177; 0.1 Program: . . . &quot;C1&quot; N252 N253 (DIS,&quot; . . .&quothttp://www.wendangwang.com/doc/efe960bed681037ac6d62544;) N254 F. . S. . T23.23 M6 . . . N267 (DIS,&quot;CHECK PLANE DIMENSION 80&quot;) N268 T30.30 M6 N269 GX150 Y35 N270 G72 Z-80 E30 N271 (GTO,C2,E30 &lt;-80.1) N272 (GTO,C3,E30&gt;-79.9) N273 (DIS,&quot;WORKPIECE IN TOLERANCE&quot;) . . . N2100 M30 &quot;C2&quot; N2101 (DIS,E30) N2102 M00 &quot;C3&quot; N2103 (DIS,E30) N2104 E31=-80-E30 N2105 (RQT,23,23,LE31) N2106 (GTO,C1);Probe on spindle ;XY positioning on the point to be checked ;Distance measured and stored in E30 ;Branch to C2 if E30 &lt; min coordinate ;Branch to C3 if E30 &gt; max coordinate;Dimension too long ;Dimension too short ;Variance between virtual and actual dimension ;Requalify length offset 23 (Z)45004457K291

Prima Electro S.p.A.Type of manual11.9OPERATIONS THAT USE A FIXED PROBEWhen you use the G74 probing cycle with a probe that is fixed in position (like an electronic gauge) and a tool mounted on the spindle, you can: requalify toolshttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 (automatic tool offset modifications) check tool wear. Example 1: This is an example of tool length offset requalification: N170 G X100 Y100 ;Positioning on the measuring point (probe position) N180 G74 Z-50 E30 ;Deviation measured and value stored in E30 N190 (RQT,10,1,LE30) ;Requalification of offset 1 for tool 10 in length (Z) by E30 Example 2: This is an example of tool length offset and tool diameter offset modification. N200 G X100 Y100 ;Positioning on the measuring point (probe position) N210 G74 Z-50 E30 ;Measured deviation (Z axis and value stored in E30) N220 G X150 N230 Z-60 N240 G74 X130 E31 ;Measured deviation (X axis) and value stored in E31 N250 E31=E31*2 N260 (RQT,10,1,LE30,dE31) ;Requalify offset 1 of tool 10 in length (Z) by E30 and in diameter (d) by E31 Example 3: This is an example of tool wear inspection with probe error management (Error management methods are described in Appendix C): N480 (DIS,&quot;TOOL Dhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544=10&quot;) N490 T10.10M6 ..... ..... N600 (DPP,10,5,500) N610 (UAO,9) N620 GXY N630 ERR=1 ;Error managed by program N640 G74 Z0 E35 ;Tool length measurement N650 (GTO,A2,STE=1) ;Branch to A2 if tool is broken (no point probed within the ;5 mm safety distance) N660 ERR=0 ;Error managed by system ..... N1500 M30 &quot;A2&quot; N2001 (TOU,10) ;Declares tool 10 out of use N2002 (DIS, &quot;TOOL K.O.&quot;) N2003 M045004457K292

Prima Electro S.p.A.Type of manual12. 屏幕管理12.1视图查看本章节介绍了一系列让你可以显示加工程序或者变量的一些命令，如下： 命令 UGS CGS DGS DIS 作用 启用一个显示范围 清空一个显示范围 取消一个显示范围 显示一个变量值12.2UGS (UCG) – 采用显示范围 (配合 Machine plot 使用)UGS 是规划了一个显示范围以便于查看加工图像。 句法 (UGS [,ax-orient],abs-axis,val1,val2,ord-axis,val3,val4 [,third-axis])其中： ax-orient abs-axis 表示坐标的方向，如下图所示有四种坐标排列，默认值是 1。 横坐标名称val1 横坐标下极限 val2 横坐标上极限 ord-axis 纵坐标名称 val3 纵坐标下极限 val4 纵坐标上极限 third-axis 第三轴的名称（通常为主轴所在的轴）213445004457K293

Prima Electhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ro S.p.A.Type of manual坐标方向类型 示例：(UGS,1,X,100,150,Y,50,250,Z) 个显示范围是横坐标方向的 X100 到 X150，纵坐标方向的 Y50 到 Y250。45004457K294

Prima Electro S.p.A.Type of manual12.3句法UGS (UCG) -三维图像显示范围(UGS ,5,axis1,val1,val2,axis2,val3,val4,axis3,val5,val6 [ , ])其中： 5 axis1,axis2,axis3 val1,val2 val3,val4     注意：   和   参数是可选的，如果他们被删除，那么系统默认值将会是如下：   = 30&#176;   = 30&#176; 表示选择了 3D 的显示模式 指定三个轴的名称 第一轴的上下极限 第二轴的上下极限 表示三维坐标系中的水平面旋转角度，典型的是 XY 平面。 表示三维坐标系中的垂直面旋转角度， 典型的是 XZ 平面。12.4CGS (CLG) -清除显示范围CGS 命令会清除平面中的加工图像但留下坐标显示。 句法 (CGS)12.5DGS (DCG) – 取消显示范围DGS 命令会取消显示范围，删除已显示的加工图像，并且移除坐标显示。 句法 (DGS)45004457K295

Prima Electro S.p.A.Type of manual12.6DIS – 显示一个变量值DIS 命令允许一个变量显示在屏幕上。 句法 (DIS,operand [,operand ] [,operand] [,operand] [,operand ])其中： operand 不能超过 80 它可以是一个数值，变量或者 ASCII 字符，多达 5 个操作对象可以被显示，所有 5 个操作对象 个字符长度。如果显示对象是一个数值，那么它的范围要在标准的范围，即小数点前五位和小数点后五位。 如果操作对象是一个变量那么它可以是任何一个变量。 如果操作对象是 ASChttp://www.wendangwang.com/doc/efe960bed681037ac6d62544II 字符，目的用来显示一条信息，这个信息最多长 80 个字符，而且字符要用双引 号 “括起来。”示例： (DIS,100) (DIS,E27) (DIS,VEF) (DIS,&quot;THIS IS AN EXAMPLE&quot;) 显示 100 这个数字 把 E27 的数值显示在屏幕上 显示当前 VEF 的值 显示这个字符串： THIS IS AN EXAMPLE45004457K296

Prima Electro S.p.A.Type of manual13. 修改程序的执行顺序13.1 13.2 13.3 总括这一章节讨论的是一些让你能够修改程序执行顺序的指令： 重复执行一段程序 执行子程序 修改程序的流程 延时和禁止 释放程序或者挂起程序执行 定义文件访问操作重复执行一段程序这些指令是允许数次去执行一系列程序段，经常用于一些重复加工操作中，例如钻若干个相同的孔。 指令 RPT ERP 定义重复循环的开头 定义重复循环的结尾 用途用于执行子程序的指令这一类指令如下： 指令 CLS PTH 作用 调用一个子程序 定义子程序的存放路径 一个子程序是由一组程序段组成的用来定义一个加工过程。子程序自己本身是一个独立的文件并有自己的名 字。当读到 CLS 时候控制器会转到该子程序并执行。子程序可以在任何位置任何时候被调用。修改程序流程的指令这类指令如下： 指令 EPP EPB GTO IF ELSE ENDIF 作用执行一段由标记符括起来的程序 执行一个程序段 实现跳跃或者转到某个位置继续执行 条件转向 GTO 指令使得执行顺序跳到一个标记符所在的位置，这个跳跃可能是无条件的或者是有条件的，基于 E 变量， 逻辑 PLC 或者一些数值延时和禁止这一类指令如下： 指令 DLY 在程序执行过程中进行延时 DSB 禁用斜杠开头的程序段 作用45004457K297

Prima Electro S.p.A.Type of manual有时候出于同步的考虑，需要在程序执行过程中加入延时。45004457K298

http://www.wendangwang.com/doc/efe960bed681037ac6d62544Prima Electro S.p.A.Type of manualCommands for the releasing or suspending the execution of a program The commands in this class are : COMMAND FUNCTION REL Releases the part-program WOS Puts the program in wait mode until a signal is received Commands for device definition The commands in this class are: COMMAND FUNCTION GDV Defines the remote device or drive A for file access operations RDV Releases the device defined with GDV These commands define the remote devices or drive A and are used when read/write operations are performed on the file via the language ASSET.程序重复执行指令   RPT - ERP The RPT and ERP commands define a set of part program blocks that must be executed a specified number of times. The set of blocks begins with the RPT command and ends with the ERP command. 语法 (RPT,n) . . Blocks . . (ERP) 其中： nIs the number of times the specified block must be executed. It is an integer from 1 to 65535 that can be programmed http://www.wendangwang.com/doc/efe960bed681037ac6d62544directly with a number or indirectly with an E parameter. The control allows five nesting levels, i.e. in a repeat block you can program up to four repeat commands. It is the set of blocks that must be executed n times. The GTO command can be programmed inside an RPT-ERP section. However, if at program end all the cycles programmed with RPT are not executed, the system returns the following error: 'NC063 RPT/ERP CYCLE OPEN AT END OF PROGRAM'.blocksIMPORTANT45004457K299

Prima Electro S.p.A.Type of manualExample 1: The following is an example of repeat command.Y 80 804020302020XProgram: (UGS,X,-50,100,Y,-50,100) (DIS,&quot;N.3 POCKETS&quot;) (DIS,&quot;MILL D12&quot;) N1 S600 T6.6 M6 N2 (RPT,3) N3 X40 Y35 M3 N4 Z 2 N5 (RPT,2) N6 G91 Z-8 N7 G90 G1 G41 X40 Y20 F300 N8 X60 N9 Y50 N10 X20 N11 Y20 N12 G40 X40 N13 Y35 F1000 N14 (ERP) N15 G Z2 N16 (UIO,X80,Y20) N17 (ERP) N18 (UAO,0) N19 Z20 N20 X Y M30http://www.wendangwang.com/doc/efe960bed681037ac6d6254445004457K20300

Prima Electro S.p.A.Type of manualExample 2: This example shows how three repeat levels are nested. (RPT, 8) (RPT, 10) (RPT, 5) 1 (ERP) (ERP) (ERP) 2 3Machining Equidistant Holes The following example uses a repeat command for machining equidistant holes.Y508 holes, path 10 10 10 0 X 0 10 80Program: (UGS,X,-50,100,Y,-50,100) (DIS,&quot;EQUIDISTANT HOLES&quot;) N1 F200 S900 T1.1 M6 N2 G81 R5 Z-10 M3 N3 X10 Y10 N4 (RPT,7) N5 G91 X10 N6 (ERP) N7 Y40 N8 (RPT,7) N9 X-10 N10 (ERP) N11 G80 G90 XY M545004457K301

Prima Electro S.p.A.Type of manual  Machining with Roughing and Finishing Cuts The following example shows repeat commands for machining with one roughing cut and one finishing cut.Finishing Cy cle Roughing Cy cleProgram: (UGS,X,-20,150,Y,-65,60) (DIS,&quot;DEFINITION OF MACHINING ALLOWANCE&quot;) N1 S350 T6.6 M6 N2 X60 Y M3 N3 Z-50 N4 MSA=0.5 N5 (RPT,2) N6 G1 Ghttp://www.wendangwang.com/doc/efe960bed681037ac6d6254441 X60 Y60 F500 N7 G3 Y-60 I60 J N8 G1 X100 N9 G3 Y60 I100J N10 G1 G40 X60 N11 MSA=0 N12 (ERP) N13 GZ20 M5 N14 X Y M3045004457K302

Prima Electro S.p.A.Type of manual  COMMANDS FOR SUBROUTINE EXECUTION   CLS - Call Subroutine The CLS command calls and executes a subroutine that is stored in a file. The routine can be called by the main program or by another subroutine. You can nest up to four subroutine levels. 语法 (CLS,name) 其中： name Subroutine file name. name must be specified by a string of upper-case characters, or a string variable preceded by the key &quot;?&quot; (question mark). In this case, the subroutine is not analyzed on activation of the main part program but while the latter is in execution. This means that the subroutines in question must not contain jump instructions. name may be a 10 SERIES type name (40 alphanumeric characters) or a file with DOS type name (8 characters plus extension and path)http://www.wendangwang.com/doc/efe960bed681037ac6d62544. Example: (CLS,E:.PRG) ;call to subroutine with DOS name Example: (CLS,PROGRAM.MIO) NOTE: If the MAIN is a 10 SERIES directory (with file names of 48 characters) the subroutine cannot be resident in a DOS directory, and accordingly three-letter code CLS cannot specify a complete path. The pathname to use for calls to subroutines in a DOS directory may also be declared through the threeletter code PTH described later in this chapter. If the pathname is omitted the directory search for the subroutine is carried out as follows : 1. No pathname specified via PTH   The system searches for the subroutine in the directory in which the calling program is found and if it is not there, it looks in the DOS directories to which logical names have been associated during the characterisation phase of the machine. 2. Pathname specified via the PTH instruction   The system looks for the subroutine in the directory specified with PTH,http://www.wendangwang.com/doc/efe960bed681037ac6d62544 if it is not there, it looks in the DOS directories to which logical names have been associated.45004457K303

Prima Electro S.p.A.Type of manualExample 1: The following is an example of a call to a subroutine. Main program Subroutine P800 N16 . . . N17(CLS,P800)N N500. . . 18. . . N501. . . . N502. . . . N503 . . . N67(CLS,P800)N 68 . . . Example 2: Sequence for execution of four nested subroutines.MAIN PROGRAM ........... ........... (CLS,SUB1) ........... (CLS,SUB2) ........... ........... ........... (CLS,SUB3) ........... ........... ........... ........... ........... ........... SUBROUTINE 4 ........... (CLS,SUB4) ........... ........... ........... SUBROUTINE 3 ........... ........... SUBROUTINE 2 SUBROUTINE 1........... ........... ........... ...........Example 3: Call to subroutine specified in implicit mode SC0.5=&quot;PIPPO&quot; (CLS,?SC0.5)45004457K304

Prima Electro S.p.A.Thttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ype of manualExample 4: This example uses subroutines for repeated drilling operations.Y156050202520X30Main Program: N19 (DIS,&quot;...&quot;) N20 S2000 F180 T2.02M6 N21 (UTO,1,X-20,Y-25) N22 (CLS,S600) N23 (UTO,1,X-15,Y50) N24 (CLS,S600) N25 (UTO,1,X60,Y20) N26 (CLS,S600) N27 Z015Subroutine S600 N501 N502 N503 N504 N505 N506 G81 R-108 Z-130 M3 XY Y-15 X30 Y0 G8045004457K305

Prima Electro S.p.A.Type of manualExample 5: Parabolic profile programming with a parametric subroutine. Main Program: ;N10 MAIN PAR N20 T1.1M6 S1000 M3 F700 N30 E30=72.795 ;start X N40 E31=24.28 ;focal length (twice the focus) N50 E32=2 ;Y increment N60 E33=108.24 ;start Y N70 E34=0 ;final Y N80 GX0 Y120 N90 (CLS,PAR) Subprogram PAR: ;N500 PAR ;N501 Parametric subroutine: Complete parabola execution, internal profile. N502 G1 G42 XE30 YE33 N503 E36 = E33 &quot;START&quot; N504 N505 E36=E36-E32 N506 (GTO,END,E36&lt;http://www.wendangwang.com/doc/efe960bed681037ac6d62544E34) N507 E35=SQR( 2*E31*ABS(E36)) N508 XE35 YE36 N509 (GTO,START) &quot;END&quot; N510 N511 E35=SQR (2*E31*ABS(E34))1 0 0-1 0 0 - 1 N512 XE35 YE34 00 100 ;N513 Second part of the parabola. N514 E42=E32 N515 E43=E34 N516 E44=E33 N517 XE35 YE43 &quot;START2&quot; N518 N519 E43=E43 E42 N520 (GTO,END2,E43&gt;E44) N521 E35= -(SQR (2*E31*ABS(E43))) N522 XE35 YE43 N523 (GTO,START2) &quot;END2&quot; N524 N525 E35= - (SQR(2*E31*ABS(E44))) N526 G40 XE35 YE44 N527 GX045004457K306

Prima Electro S.p.A.Type of manual  PTH - Declaration of the default pathname The PTH command declares the pathname to be used as the default in calls to subroutines and paramacros with DOS names. 语法 (PTH,mode [,pathname]) 其中： mode mode may have the following values and significance: mode=0 Taken as the default pathname for CLS calls, the path of the main program. mode=1 Declares the path to use when there is a (PTH,2) instruction active. Thhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544is mode may be of use when a pathname defined initially with (PTH,1,pathname) has to be called numerous times in the part program with (PTH,2). mode=2 Activates the path specified in the instruction or, if none is specified, the one declared previously with a (PTH,1,pathname) instruction. pathname Path to be declared as the path for CLS calls; this is an optional parameter. NOTE: The pathname declared with three-letter code PTH is preserved even after a RESET of the process in which it was programmed.45004457K307

Prima Electro S.p.A.Type of manual  EPP - Executing a Portion of a Program The EPP command allows you to execute a subprogram, i.e. a portion of a program delimited by two blocks with label fields. 语法 (EPP,label1,label2) 其中： label1 Label field of the first block to be executed. A label is a sequence of up to six alphanumeric characters. label2 Label field of the last subprogram block. 说明： Program the bhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544lock label between quotes (&quot;LABEL1&quot;) even if in EPP they must be declared without quotes. The system accepts up to 5 nesting levels. In contouring operations, you can use the EPP command for finish milling with the same program blocks you wrote for roughing. During the roughing phase, use the MSA command to program the machining allowance for finishing. In positioning operations, you can program points for a centring operation, then use the EPP command to call for different tools in order to execute different operations on each hole. The EPP command can be used to execute a complete machining operation at different orientations on the active interpolation plane. Example 1: . . &quot;START&quot;N25 First block with label . . An EPP cannot occur here . &quot;END&quot;N100 Last block with label . . . N150 (EPP,START,END) EPP command that specifies the labels. The control executes blocks N25 to N100; after this point you musthttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 resume execution with the block written after EPP (N150). The 'NC062 NESTING OF EPP &gt; 5' error occurs if more than five instructions are IMPORTANT nested in an EPP command. The GTO command can be programmed inside an EPP section. However, if at program end all the cycles programmed with RPT are not executed, the system returns the following error: 'NC063 RPT/EPP CYCLE OPEN AT END OF PROGRAM'. Example 2: This example shows how to use the EPP command in a positioning operation:Program: (UGS,X,-110,110,Y,-110,110)45004457K308

Prima Electro S.p.A.Type of manualN1 (DIS,&quot;DRILLING CENTRE HOLES&quot;) N2 F300 S2000 T1.1 M3 M6 N3 G81 R0 Z-3 &quot;D6&quot;N4 N5 X100 Y100 N6 X-100 N7 Y-100 N8 X100 &quot;D10&quot;N9 N10 X40 Y40 N11 X-40 N12 Y-40 N13 X40 &quot;END&quot;N14 N15 G80 N16 (DIS,&quot;BIT D6&quot;) N17 F200 S1800 T2.02 M3 M6 N18 G81 R Z-22 N19 (EPP,D6,D10) N20 G80 N21 (DIS,&quot;BIT D10&quot;) N22 F220http://www.wendangwang.com/doc/efe960bed681037ac6d62544 S1600 T3.3 M3 M6 N23 G81 R Z-24 N24 (EPP,D10,END) N25 G8045004457K309

Prima Electro S.p.A.Type of manual EPB - Execute Part-Program BlockThe three-letter code EPB allows execution of a part-program block. Execution can be conditioned by the result of a comparison specified within the command; If the condition is not met an alternate part-program block may be defined so as it can be executed. 语法 (EPB, part_program_block1 [ , par1 operator par2 [ , part_program_block2 ] ) 其中： part_program_block1 Is the part-program block to be executed. This can be a string in inverted commas or a character, local or system variable. par1 Is a local or system variable or a constant whose value is compared to the value contained in the par2 parameter. operator Logic operators which can be used in the expressions : = equal to &lt; less than &gt; greater than &lt;&gt; not equal to &lt;= less than or equal to &gt;= greater than http://www.wendangwang.com/doc/efe960bed681037ac6d62544or equal to par2 Is a local or system variable or a constant whose value is compared to the value in the parameter par1. part_program_block2 Is the block of the part-program to execute only if the specified condition for part_program_block1 is not met. It is an optional parameter. This can be a string in inverted commas or a character, local or system variable. 说明： If par1 ,operator and par2 conditions are not specified, the program executes the part_program_block1 block. Only one level of nesting is accepted by the system with the three-letter code EPB.45004457K310

Prima Electro S.p.A.Type of manualExample: (EPB, “(EPB,’E1=1’)”) : accepted by the system (EPB, “(EPB,’(EPB,SC0.100)’ )”) : NOT accepted by the system (error: FORMAT ERROR) The part-program blocks specified in the three-letter code EPB are not analyzed in the activation phase of the part-program, therefore it is up to the programmer to see that theshttp://www.wendangwang.com/doc/efe960bed681037ac6d62544e blocks do not cause any malfunctioning of the part-program. Example: (EPB,”(CLS,SUBROUT)”) : the subprogram SUBROUT is not pre-analyzed in the activation phase, therefore it cannot contain any jump (GTO) instructions. (EPB,’ “LABEL” ’) : The label LABEL will not be inserted in the label table of the part-program. (EPB, “ ( DIS, E1)” ) : equivalent to the block (DIS, E1) SC0.30= ” E1 =10” (EPB, SC0.30) : equivalent to the block E1=10 SC40.30 = “# X10” (EPB, SC40.30) : equivalent to the block #X10 (EPB,”(CLS,SUBROUT)”,E1=34) : calls the subprogram SUBROUT only if E1=34 (EPB,” E1=100”, SN1=25,” E1=0”) : assigns 100 to E1 only if SN1=25, otherwise assigns 0 to E1 (EPB,”(EPP,LAB1,LAB2)“,SC0.2=“OK”,“(EPP,LAB3,LAB4)“) : executes from the label LAB1 to the label LAB2 if SC0.2 is equal to OK, otherwise executes from the label LAB3 to the label LAB4. (EPB, “( EPB,’ E1 = 2’, E0 &lt; 100)”, E0 &gt; 70 ) : assigns 2 to E1 only if E0 is betweehttp://www.wendangwang.com/doc/efe960bed681037ac6d62544n 70 and 100. (EPB,“ ( EPB,’ E0 = 5’, E0 &lt; 5) &quot;,E0 &lt; 10,E0=10) : assigns the value 5 to E0, if E0&lt;5; assigns 10 to E0 if E0&gt;10. If 5&lt;E0&lt;0, E0 does not change.45004457K311

Prima Electro S.p.A.Type of manual  BRANCHING AND DELAY COMMANDS. SLASHED BLOCKS   GTO - Branch Command The GTO command performs a jump to the specified block if the condition expressed in the command is true. 语法 (GTO,label [,par1 operator par2]) 其中： label Label of the program block to branch to. A label is a string of up to 6 alphanumeric characters. In the destination block the label must be between quotes while in GTO command the label must be programmed without quotes. Also, the label can be a character variable preceded by “?” par1 It is the local or system variable whose value is compared to the value of the par2 variable. operator Logical operators that can be used in expressions: = equal &lt; less than &gt; greathttp://www.wendangwang.com/doc/efe960bed681037ac6d62544er than &lt;&gt; different than &lt;= less than or equal to &gt;= greater than or equal to par2 It is the local or system variable whose value is compared to the value of the par1 variable. 说明： If par1, operator and par2 are not specified, the program always jumps to the block marked by the label. The label the part program must branch to can also be expressed as a local or system variable (preceded by the &quot;?&quot; character). This facilitates execution of programs having a great number of blocks. In particular, by programming the label as a variable it is possible to program a default label and call it &quot;DEFLAB&quot;: The part program positions on &quot;DEFLAB&quot; if the label in the variable does not exist.45004457K312

Prima Electro S.p.A.Type of manualExample 1: ;SC0.3 contains the positioning label (GTO,?SC0.3) &quot;ONE&quot; . . . . &quot;TWO&quot; . . . . &quot;THREE&quot; . . . &quot;DEFLAB&qhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544uot; . . . If SC0.3 does not contain &quot;ONE&quot;, &quot;TWO&quot; OR &quot;THREE&quot; the part program positions on the &quot;DEFLAB&quot; block. If the &quot;DEFLAB&quot; label exists, the 'NC054 Undefined label' error is displayed and part program execution is interrupted. Example 2: N01 (GTO,START) the part program always branches to &quot;START&quot; N10 (GTO,END,E1 &gt; 123) branch to &quot;END&quot; if the value of E1 is greater than 123 N20 (GTO,LAB1,@COOLANT = 1) branch to &quot;LAB1&quot; if the PLUS variable @COOLANT is on N30 (GTO,START,E1 &lt;&gt; E5) branch to &quot;START&quot; if the value of E1 is different from that of E5 N40 (GTO,LAB1,SC1.2 = &quot;OK&quot;) branch to &quot;LAB1&quot; if the two characters beginning with SC1 are equal to OK N50 SC1.3=&quot;ABC&quot; prepares the variable for the following block N60 (GTO,?SC1.3) branch to ABC label Example 3: The instruction: (GTO,END,SC2.3 = &quot;ABC&quot;) bhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544ranches to the &quot;END&quot; label in the program if the three characters (.3) beginning from SC2 are ABC. NOTE: The character string to be compared in the branch command must always be programmed between quotes.45004457K313

Prima Electro S.p.A.Type of manualExample 4: Here is an example of conditional branching in slot milling.Program: (UGS,X,-50,50,Y,-50,50) N1 (DIS,&quot;MILL A SLOT&quot;) N2 F500 S2000 T1.1 M3 M6 N3 E31=-3.5 N4 E32=-24 &quot;START&quot; N6 G X Y-10 N7 Z(E31) N8 G1 G42 X Y-20 N9 X-30 N10 Y20 N11 X30 N12 Y-20 N13 G40 X N14 Y-10 &quot;END&quot; N16 E31=E31-3.5 N17 (GTO,START,E31&gt;E32) N18 E31=-25 N19 (EPP,START,END) N20 G Z1045004457K314

Prima Electro S.p.A.Type of manualExample 5: This is an example conditional branching in cylindrical thread machining.E30 E31 E32 E33= = = =Diameter of Next Cut Cut Depth Increment (Diameter) Return Diameter Final DiameterProhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544gram: N1 (DIS,&quot;THREAD DIA 60&quot;) N2 S150 T5.5 M6 N3 G0 X66 Y98 Z5 M3 N4 E30=56.8 N5 E31=0.5 N6 E32=50 N7 E33=60 &quot;I&quot; N8 N9 G0 Z5 N10 U(E30) N11 G33 Z-45 K3 N12 GU(E32) N13 E30=E30 E31 N14 (GTO,F,E30&gt;E33) N15 (GTO,I) &quot;F&quot; N16 N17 GU(E32) N18 Z5 N19 U(E33) N20 G33 Z-45 K3 N21 GU(E32) N22 Z2045004457K315

Prima Electro S.p.A.Type of manual  IF ELSE ENDIF The IF command allows the opening of a part-program session which will be executed only if a condition specified within the command is met. This part-program session must terminate with the ENDIF command : the ELSE command can be optionally included in the IF command, which delimits, up until the ENDIF command, a part-program session which will be executed if the condition specified in the IF command is not met. 语法 ( IF, par1 operator par2 ) (ELSE) (ENDIF) 其中： par1 Is a local or system variable or a constant whose value will be comparedhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 with the par2 parameter. operator Logic operators which can be used in the expressions : = equal to &lt; less than &gt; greater than &lt;&gt; not equal to &lt;= less than or equal to &gt;= greater than or equal to par2 Is a local or system variable or a constant whose value is compared to the value in the parameter par1. Characteristics. If the condition specified in the IF command is met, the blocks specified up until the ELSE command (if present) or until the ENDIF command (if the ELSE command is not present) will be executed, otherwise they will be ignored. The blocks between the ELSE command and the ENDIF command will be executed only if the condition specified in the IF command is not met. 5 levels of nesting are allowed with the IF ELSE ENDIF command. Every IF command must have a corresponding ENDIF command.45004457K316

Prima Electro S.p.A.Type of manualExamples: ( INP,” E0 VALUE “ ,30 , E0) ( IF , E0 = http://www.wendangwang.com/doc/efe960bed681037ac6d625443) ( DIS , “ E0 is equal to 3 “) (ELSE) ( IF E0 &gt; 3) ( DIS , “ E0 is greater than 3 “) (ELSE) ( DIS , “ E0 is less than 3 “) ( ENDIF) ( ENDIF) ( INP,” E0 VALUE“ ,30 , E0) ( IF , E0 &gt;10 ) ( IF , E0 &gt;20 ) ( IF , E0 &gt;30 ) ( IF , E0 &gt;40 ) ( IF , E0 &gt;50 ) ( DIS , “ E0 is greater than 50 “) ( ENDIF) ( ENDIF) ( ENDIF) ( ENDIF) ( ENDIF)   DLY - Defining Delay Time The DLY command specifies a delay in program execution. 语法 (DLY,time) 其中： time Delay time in seconds (minimum value 0.1). You can program the delay with a numerical constant or an E parameter.45004457K317

Prima Electro S.p.A.Type of manual  DSB - Disable Slashed Blocks This command enables/disables slashed blocks. Slashed blocks have &quot;/&quot; symbol as first character and their execution is conditioned by the DBS value. 语法 DSB= value 其中： value The value may be: DSB=0 slashed blocks are executed DSB=1 slashed blocks are not executed   REhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544L - Releasing the part program The REL command releases the part program and all subroutines. 语法 (REL) 说明： The REL function disables the part program. It can be entered through MDI. After the program has been released, the following message will be displayed: 'NC058 END OF PROGRAM'.45004457K318

Prima Electro S.p.A.Type of manual  WOS - WAIT on signal 语法 (WOS,par1 operator par2) 其中： par1 Is a local or system variable or a constant to be compared to the value of par2. operator Logic operators that can be used in expressions: = equal to &lt; lower than &gt; higher than &lt;&gt; different than &lt;= lower or equal to &gt;= higher or equal to par2 Is a local or system variable or a constant to be compared to the value of par1. 说明： The process where the WOS function is programmed goes on WAIT until the condition is satisfied. By default the WOS command is synchronised. If the system is on WAIT during program debugginhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544g (because a WOS function has been programmed), it is possible to assign to the par1 variable the value that satisfies the condition specified in WOS. To make this assignment, follow these steps:   Press CYCLE STOP   Key in the correct value of the par1 variable.   Press CYCLE STOP Example: (WOS,E1&gt;4) (WOS,SC10.5 = &quot;GOOFY&quot;) (WOS, TOOL_STATUS&gt;=E3) (WOS,!USER_VAR3.5CH 0 SC4.5)45004457K319

Prima Electro S.p.A.Type of manual  DEVICE DEFINING COMMANDS   GDV - Definition of the device for file access This three-letter code is used to reserve use of drive A for file read/write operations and to define remote devices on which to work. 语法 (GDV, device) 其中： device Name of device. May be a letter or, if preceded by a &quot;?&quot; key, a local or system variable specifying the drive to be used. For the floppy drive, the letter &quot;A&quot; must be used as the identifier. For remote devices, the name to behttp://www.wendangwang.com/doc/efe960bed681037ac6d62544 given is that with which it was defined with the option MINI DNC E65/E66 (e.g. &quot;K&quot;). 说明： If drive A is already being used by another process or UTILITY (e.g. DOS SHELL), the error NC251 Driver busy or not configured is generated; this error can be handled by the part program (for further details, refer to appendix C). Examples: (GDV,A) Reserves use of drive A. SC0.1='A' (GDV,?SC0.1) Use of drive A is reserved, as specified in variable SC0.1 A system RESET cancels access to drive A but not to remote devices.IMPORTANT45004457K320

RDV - Release device

defined previously with the three-

code GDV, so as to make it available for other users.

语法

(RDV, device)

其中：

Name of device.

be a letter or, if preceded by a ? key, a local or system variable specifying the drive to be used.

the floppy drive, the letter &quot;A&quot; must http://www.wendangwang.com/doc/efe960bed681037ac6d62544be used as the identifier.

remote devices, the name to be given is that with which it was defined with the option MINI DNC E65/E66 (e.g. &quot;K&quot;).

说明：

process reset is tantamount to automatic execution of a (RDV,A) command.

:

(RDV,A)

drive A previously allocated with GDV.

.1='A'

(RDV,?SC0.1)

to the previous example, but with the drive specified in variable SC0.1.

[此处图片未下载成功]

14. HIGH SPEED MACHINING

. MULTIPROCESS MNAGEMENET COMMANDS

. HIGH LEVEL GEOMETRIC PROGRAMMING (GTL)

. WORKING CYCLES FOR TURNING SYSTEMS

. FILTERS

to be translated

19. APPENDIX A: 字符和命令

.1 字符表

下面是被控制器识别的ASCII, EIA 和ISO字符的打孔磁带格式。注意，取决于编码，可能会有奇校验(EIA)，偶校验(ISO)或无校验(ASCII)。

[此处图片未下载成功]

Prima Electro S.p.A.

of manual://www.wendangwang.com/doc/efe960bed681037ac6d62544par

字符 D d E F G 轴名 带 GTL 的距离 刀具直径(RQP,RQT) 用于加工周期的参数 在 G1-G2-G3 中的轴进给率 预备编码(G00 - G99) 保留的(G100 - G299)

描述

子程序(G300 - G999) H h I i J j K 用于 PARAMACROS 的参数 在连续动作中的补偿值改变 在圆形插入中的弧形中心坐标(G2-G3)(横坐标) 在 G33 中的变量 PITCH 刀具范围向量(同 j 和 k) 在圆形插入中的弧形中心坐标(G2-G3)(纵坐标) 在(G83)中的最小深度增量 刀具范围向量(同 j 和 k) 在打孔周期中 I 和 J 的减少因数 线性 PITCH(G33) 线性 PITCH(G84) k L l 在螺旋插入中的螺距 刀具范围向量(同 j 和 k) 用户表变量 刀具补偿的长度 1(RQT, RQP) 刀具补偿的长度 2(RQT, RQP) 带 GTL 的直线 M m N n o P p Q R 辅助字母 表面的普通向量(同 n 和 o) 加工

程序段编号 表面的普通向量(同 m 和 o) 表面的普通向量(同 n 和 m) 带 GTL 的原点 轴名 带 GTL 的点 轴名 在周期 G81 - G89 中快速定位 从主轴 0 的偏离(用于多启动线) 在圆形插入 G02-G03 中的半径 r 轮廓半径(只用于切割直径补偿) G73 周期 带 GTL 的半径 S s 主轴速度 带 GTL 的交叉点

K

[此处图片未下载成功]

. APPENDIX B

. APPENSIX C

to be translated

[此处图片未下载成功]

发行单位: PRIMA ELECTRO S.p.A Strada Carignano, 48/2 – Moncalieri (TO)  ITALY 电话:  39 0119899800 网址: wwhttp://www.wendangwang.com/doc/efe960bed681037ac6d62544w.osai.it - http://www.wendangwang.com 电子邮件: it.sales@http://www.wendangwang.com    Copyright   2011 by PRIMA ELECTRO S.p.A.

Prima Electro S.p.A.

of manual

K

文档下载网是专业的免费文档搜索与下载网站，提供行业资料，考试资料，教学课件，学术论文，技术资料，研究报告，工作范文，资格考试，word文档，专业文献，应用文书，行业论文等文档搜索与文档下载，是您文档写作和查找参考资料的必备网站。

文档下载 https://www.wendangwang.com/

亿万文档资料，等你来发现