# REGION ONE

# CLEARWATER / NEZ PERCE NF'S

# 2006

HELICOPTER OPERATIONS

&

## SAFETY PLAN

| Prepared by: | /s/ Jeff Polack /s/ Nate Raff | Date: | 07/26/2006 |
| --- | --- | --- | --- |
|  | Jeff Polack / Nate Raff |  |  |
|  | Helitack Supervisors |  |  |
| Reviewed by: | /s/ William H. Acton | Date: | 07/20/2006 |
|  | Willy Acton |  |  |
|  | Zone Aviation Officer |  |  |
| Reviewed by: | /s/ Jim Gray | Date: | 07/27/06 |
|  | James Gray |  |  |
|  | Zone Fire Staff Officer |  |  |
| Reviewed by: | /s/ Robert L. Quirino | Date: | 07/20/06 |
|  | Bob Quirino |  |  |
|  | Region 1 HOS |  |  |
| Approved by: | /s/ Darcy Pederson | Date: | 08/01/06 |
|  | Darcy Pederson |  |  |
|  | District Ranger |  |  |
| Approved by: | /s/ Cynthia Lane | Date: | 07/20/2006 |
|  | Cynthia Lane |  |  |
|  | District Ranger |  |  |

# CLEARWATER / NEZ PERCE NF'S

# HELICOPTER OPERATIONS & SAFETY PLAN

# INTRODUCTION

This Plan establishes standard operating procedures for the Clearwater / Nez Perce Fire Zone Helicopter Program, and supplements the Clearwater/Nez Perce Aviation Management & Safety Plan.  This plan is also a stand-alone briefing document for Zone users and helicopter personnel assigned to the Clearwater/Nez Perce Zone. Contents of this plan include personnel, equipment, operational procedures, and safety.  Appendices contain additional information that is useful while operating on the zone.   All Zone helicopter personnel shall become familiar with the contents of this plan.

# PURPOSE

To acknowledge and follow established policy and procedure for safe, effective  and efficient use of helicopters on the Clearwater and Nez Perce National Forests.  Aviation Safety is incorporated by the procedures, methods and references throughout this plan.

Air Operations and Safety Guidelines are outlined in the R1 and R4 Aviation Management Plan, Aviation Mishap Prevention Plan, FSM 5700, FS Health and Safety Code, Interagency Helicopter Operations Guide, Federal Aviation Regulations, Federal Aviation Manuals, the Interagency Aerial Ignition Guide, Interagency Helicopter Rappel Guide, the Clearwater / Nez Perce National Forests Aviation Management and Safety Plan, and the helicopter contract provisions.

The Zone Helicopter Program provides services in the following areas for the resource and fire management programs within the  Clearwater/Nez Perce Zone, Region One, Nationally and for Interagency Cooperators:

Wildland Fire Initial/Extended attack/logistical support

Management of CWN Helicopters

Wildland Fire Use

Prescribed Fire

Project Work

Comprehensive Aviation Training Programs

Service delivery is anchored on SAFETY, EFFECTIVENESS AND EFFICIENCY.

Grangeville Helitack Crew

Musselshell Helitack Crew

At time of hire, and/or within 60 days, all personnel must meet or exceed air operations qualifications as outlined in the Interagency Helicopter Operations Guide, FSHB 5109.17,Chapter 40 and meet WCT physical requirements at the arduous level.

Target qualifications for the Helicopter Program will include:

Helitack Supervisors (ICT3/DIVS, RXB2, ASGS)

Assistant Supervisor (TFLD, STCR, RXI1, HEB1)

Squad Leader (CRWB, FEMO/FOBS, HEB2, FALC, HCWN)

Crewmember (FFT1, ICT5, FEMO, FALB)

Helitack Crew Role

The role of the Helitack Crews is to provide logistical and tactical support to the Clearwater – Nez Perce Fire Zone in the areas of resource management, aerial igniton for prescribed fire, suppression of fires, training for helicopter operations, Fire Use activities and to maintain helicopter readiness and proficiency. The operational use of the Helitack crew and helicopter may be determined by the requesting unit and/or IC of the incident. At times the District will request the Helitack crew to fly directly to the fire to function as initial attack firefighters. The helicopter manager and /or helitack crewmember(s) may be available to stay on the incident to function as IC or other specialized position needed on the fire.

Standard Configuration:  The standard configuration  will include a qualified exclusive use helicopter manager and two helicopter crewmembers/firefighters. The two crewmembers will include an ICT5 and a FALB at a minimum.  Crewmembers will be equipped with tools, food, water, water filter and sleeping bag, adequate to be self sufficient for a 36-hour period.  Personnel will be prepared to hike to a road or landing site upon declaring the fire out.      When a second manager is available, the manager on board will be available to function as ICT4 or fill other specialized positions during more complex operations.

Standard equipment on the aircraft will include personal initial attack gear, three hand tools, chainsaw with accessories, and bambi bucket. Helicopter remote hook is not part of the standard load and will normally be kept on support vehicles.   The standard load may be modified by the helicopter manager when necessary to meet performance limitations of the aircraft for landings at unknown helispots using the Hover-Out-Of Ground allowable payload or when the mission type dictates a change. A HOGE power assurance check is to be accomplished prior to  initial off site landings ( for example the first trip into a helispot on an initial attack) at an altitude comparable to the site or greater.  A positive  rate of climb must be established without exceeding aircraft limitations.

Support vehicles will be equipped with additional tools and equipment for extended assignments. To provide adequate mission support, the deployment of support vehicles will be at the helicopter manager’s discretion upon consultation with Grangeville Interagency Dispatcher and the District Duty Officer.

Availability:  The Grangeville helicopter is on contract for 100 days and will start on June 22, 2006.  The Musselshell helicopter has a 90 day availability period and will start on June 26, 2006. Standard duty hours for the pilot will be 0800-1700.  Daily availability hours may be adjusted to meet incident needs as long as pilot duty limitations are not exceeded.

Staffing and Readiness:  While the aircraft are on contract, the modules will work split workweeks and provide seven day coverage. A minimum of three persons will staff the helicopter each day.    The minimum coverage level will be one manager and two crewmembers. The full crew will be on at least one common day each week for training.

Any helicopter managers used to supplement the management of the Exclusive Use helicopters on the Zone shall be approved by the Zone Aviation Officer or designee (for example,  using a Call When Needed helicopter manager or helicopter manager from another Exclusive Use crew to cover days off for a Zone helicopter manager).

The District Duty Officer will provide Grangeville Interagency Dispatch Center with a daily staffing report that will include qualifications of crewmembers.  Aircraft status will be reported by Grangeville Interagency Dispatch Center during the morning weather.  Requests for specialized positions (e.g. FALC, EMT, ICT4) and equipment ( longline, extra fuel, crosscut saw ) shall be placed with aircraft requests.  Dispatch will coordinate with the Helibase to fulfill these requests whenever possible.  Crewmembers in excess of minimum staffing levels will be made available for off forest fire assignments, CWN aircraft management and project work. This will include extended duration assignments at remote areas unless actual and predicted fire activity dictates otherwise. All personnel will be prepared to respond to wildland fire from any project site within 30 minutes.

Each morning the assigned crew will be identified and the helicopter will be loaded with their personal initial attack gear.  Takeoff will normally occur within 10 minutes of final dispatch instructions but should not exceed 15 minutes. Any delay in the response shall be communicated to dispatch. Request for specialized personnel or equipment may cause delays in response times.

DAILY SCHEDULE:

The intent of the daily schedule is to create a base level of expectations of the routines and timeframes to be followed on both of the helibases. Any significant deviation from the schedule shall be cleared through the Zone Aviation Officer. Occasional spot checks of the routine should be expected.

0800-0815:

- Foreman: Call Dispatch Office for any pending missions and crew staffing update. Confirm how many people are available for IA and capabilities

- Ensure that there is an ICT5 and FALB on each IA load for the day

- Load Calculation/Manifests completed and signed. All loads for unknown landing areas shall be done using HOGE performance. A manifest for the bucket shall be completed.

- Check with Dispatch for project work. Also coordinate with the local FMO/Duty Officer for project work and District needs.

- Brief pilot and FSVD for day’s activities.

- Flight helmet bag, nomex shirt and portable radio on rack. Web gear and map case in A/C. Ensure pilot is pre-flighting aircraft.

- Daily Duties list updated and fire rotation list updated.

Pilot:  Load Calculation completed, Preflight A/C, tie in with Manager for mission planning ( fuel load, maintenance issues, company needs etc) nomex and boots at the ready, fuel truck moved from pad, lunch available in case of dispatch.

Fuel Service Vehicle Driver: Fuel samples completed and logged, vehicle readiness, lunch packed, mission briefing for days activities,

Crew: Manifest 1st load, load aircraft with IA gear (3 tools, web gear, saw with saw kit, bucket w/longline, etc), nomex and radios on rack, pull intell. (Weather, sit-rep, 6 Min. For Safety), chase truck inspection (daily pm check), Daily Duties list completed ( empty trash, vehicles PM checks, sweep floors, clean bathroom etc)

0815-0915: PT.

- PT for the IA team and Helicopter Manager shall be performed at GAC and will maintain a 15 minute response time if dispatched.

- If a full crew PT ( for example, the IA team and the Helicopter Manager will PT off site from the helibase and will not be able to meet a 15 response time)is approved by Grangeville Dispatch,  each individual or group shall maintain contact with either a cell phone or radio. Full and active participation by all is required regardless location of the PT (if you are too sick/sore, etc to PT, you are too sick to go on a fire).  Boots and Nomex shall be on the rack and ready to go.

0915-0930: Dress down from PT and gather for briefing from Manager.

0930-1045:

- Daily crew and flight crew briefing (status report, planned missions, intell, 6 minutes For Safety, fire weather etc)

1000-1200:

- Project work and training as assigned/needed.

- Approximately 5 minutes prior to lunch, the helicopter manager shall call the Dispatch Center to ensure there is not a pending order for the aircraft or crew. The Helicopter Manager should also inform the Dispatch Center as to how they may be contacted during lunch in case of a dispatch.

1200-1300:

- Lunch. Contract personnel must be available via radio or cell phone. It is recommended that the crew have some means of being contacted in case of dispatch. It is expected that for the duration of the helicopter contract that the crew and contractor personnel have provisions for lunch arranged daily in the event they are dispatched away from the base.

1300-1305:

- Gather crew/contractors for quick brief and ensure no changes have occurred over lunch.

1305-1630:

- Project work and training as assigned.

1630-1645: Finish project work/training. Tools away, work areas and office cleaned, vehicles cleaned and gassed, timesheets updated. Fire availability board updated. 122’s and daily diaries updated.

1645-1700: Contact Dispatch to check for pending assignments and check for assignments in the AM. Brief on days accomplishments, line out projects and assignments for the next day. Initial attack gear off ship and readied for the next day. Ensure each crewmember knows what their duties are for the next day. Call Zone Aviation Officer and update on days events, needs or issues. Ensure after hours/days off contact numbers are recorded at the base. Complete Crew Daily Diary.

1700- Call “Grangeville/Musselshell Helitack out of service”. Ensure District Duty Officer is informed on who the manager is and their contact information.

Safety and Efficiency: Utilizing risk management procedures outlined in Chapter 3 “Operational Planning” of the Interagency Helicopter Operations Guide, the helicopter manager, in consultation with the District Duty Officer, will minimize the inherent risk involved in aviation.  This will include mission planning to minimize exposure to the aircraft and personnel.  Minimizing flight time will promote efficient use of the aircraft and provide a better service to the fire Zone.  The pilot in command will have final say in accepting any mission.

Coordination and Dispatch:  Priority uses for the Helicopter Program are:

- National Security

- Protection of Life

- Protection of Property

- Protection of Resources

Helicopter requests for projects or fire will be placed through Grangeville Interagency Dispatch Center.  During the contract period, requests for the use of a helicopter or helitack personnel for fire or project work will be placed with Grangeville Interagency Dispatch and coordinated thru the District Duty Officer.   The helicopter manager will contact the requester with any specific questions.   Helitack Supervisors and Assistants will be responsible for coordinating with districts to arrange project work outside of the contract period.

Upon arrival over a fire, the assigned Incident Commander will provide Grangeville Dispatch with a fire size up, and recommend initial resource needs.  Prior to landing and dropping off firefighters, the Manager will discuss with the Incident Commander travel routes to and from the fire, as well as possible locations of safety zones and two escape routes.

Staffing CWN Aircraft:  Ability to staff CWN aircraft is dictated by the type and classification of the aircraft.  Due to the variation in the personnel requirements, the number of CWN aircraft that can be staffed by program personnel will be limited by the number of helicopter managers available.  The number of crewmembers necessary may exceed IHOG requirements if the aircraft is intended to be used for initial attack.  District personnel with helicopter qualifications or in trainee positions should be incorporated into CWN modules to provide an opportunity to maintain currency and develop new skills.

Managers shall ensure load calculations are completed, record power checks every 10 hours of flight, and keep accurate flight time readings for individual projects.  The manager will complete the pilot flight & duty record, flight invoice and daily diary at the end of each day.  Helicopter managers will notify dispatchers of any significant changes, such as crew status, staffing levels, maintenance requirements and aircraft availability, that will effect helicopter operations.  Cost Summaries should be turned in to the districts daily, to provide for accurate tracking of fire costs.  Zone aircraft flight invoices are to be sent to the Air Center on the 15th and last day of each month.  Off Zone helicopter managers operating on the Zone, are required to leave photocopies of their flight invoices with the Zone Aviation Officer or local dispatcher prior to demobilization. These reports are essential in maintaining Zone helicopter utilization records.

Personnel Expectations – All employees shall conform to the Clear/Nez Fire Zone code of conduct.  Helicopter personnel, both government and contractor employees, are professionals and are expected to exhibit their professional attitudes in the performance of their duties.  During standby or project work personnel are expected to maintain mission readiness.

# EQUIPMENT

Issued gear: Each helicopter program crewmember will be issued a web pack, a red bag, FM  radio, hardhat, goggles, gloves, headlamp etc..  Personnel will be expected to care for these items and return them once the season is over.

For commercial travel purposes, the web pack must not weigh over 20lbs. and the red pack over 45lbs..

Personnel Protective Equipment: Helicopter program personnel will be issued  Nomex shirt and pants, SPH-4/5 flight helmet, Nomex and leather gloves, hearing and eye protection to be worn during helicopter operations.  Eight inch leather boots must also be worn. Undergarments are required to be of 100% cotton.  District personnel may sign out specialized equipment necessary to perform in Call When Needed roles.

# Exceptions:

Rubber/synthetic boots may be worn if the environmental situation warrants; otherwise leather boots are required.  Approved flight helmets are required for all passengers, except firefighters when operating from an established, managed helispot/helibase to an established, managed helispot/helibase.  In that case, firefighter hardhat with chinstrap securely fastened may be used.

Helicopter:  The aircraft and pilot will usually be prepared to launch within 10 minutes of receiving dispatch instructions. The maxiamum time will be 15 minutes barring any unforseen circumstances.   Standard fuel load for the helicopter will be one and one half hour usable fuel, with one half hour of reserve fuel,  (two hours total).  On longer distance dispatches, more fuel may be added, but will not exceed the allowable payload of the aircraft.

Helicopter fuel/service vehicle: This vehicle is to be available as stated in the helicopter contract. The service truck will be dispatched at the discretion of the government when the aircraft is dispatched or re-positioned away from the designated base.

Support truck:  The USFS support truck contains equipment and supplies necessary to support fire and project operations.  The support truck will be properly maintained, equipped and fire ready. The support truck and it's contents are the responsibility of the helicopter manager assigned to the operation.  In order to drive support trucks outside of the state, operators must hold a valid medical card as required by parts 391.41 and 391.43 of the Federal Motor Carrier Safety Regulations.  All personnel must comply with driving and duty limitations outlined in the Interagency Incident Business Management Handbook.

Trauma and Evacuation kits: These kits may be available at the Air Center, for use at helibases or in emergencies as needed.  These kits will also be carried in the support trucks.

Crash rescue kit:  As required by the Interagency Helicopter Operations Guide, crash rescue kits will be available at all helibases.  Helicopter crewmembers shall be trained in the contents and use of these kits.

Specialized Equipment:  Equipment and supplies necessary for helicopter use will be maintained and kept at the Air Center and/or Musselshell Work Center.  Some of the items on hand include extra nets, swivels, leadlines, choker cables, flight helmets, 6000 gal. collapsable dip tank, 10,000 gal. Heliwell tank, filler pumps and accessories, 3 plastic sphere dispensers, 1 helitorch and a transfer pump and a 10,000 lb. capacity scale.   Some districts will also maintain basic equipment as part of their local cache.

Helicopter equipment:  All helicopter equipment shall be inspected prior to each use and before returning to storage.   All damaged or excessively worn equipment shall be tagged and removed from service.  Refer to the Interagency Helicopter Operations Guide for a list of approved equipment and inspection standards.

Remote Fuel Trailers:  Jet A fuel trailers are located at remote sites on the Zone. Currently these sites are Canyon Work Center ,Powell Ranger Station and the Dixie Airstrip/Helibase. Trailers will be well maintained and inspected pre and post season.  Prior to fueling helicopters from Forest Service tanks, a sump, filter, and nozzle check must be performed to ensure fuel quality.  Record results in Fuel Inspection Log with each site.  Aircraft pilots must visually inspect and approve fuel prior to dispensing. In the event of a fuel spill, each trailer is supplied with a spill containment kit. For large spills, from any fuel source on the Zone, contact GVC who will notify the forests hazmat coordinators.

Any additional equipment needs may be ordered from the Northern Rockies Fire Cache in Missoula,  Montana through the Grangeville Interagency Dispatch Center.

Facilities

# One Helicopter Operations Base is located at the Grangeville Air Center on the Idaho County Airport (S80) in Grangeville, Idaho.  The Air Center  also serves as a Retardant, Smokejumper, and Light Fixed Wing base.  Two 20' x 20' concrete helicopter pads, designed for Type II and Type III helicopters, are located in the field on the west side of the Air Center. Fire extinguishers, water and electricity are supplied to each pad.  A fire hydrant is on the southwest corner of the helibase.  A Tri-Max® 30 gallon Compressed Air / AFFF Foam Fire Extinguisher, hoses, nozzles, power cords and halogen lights and stands are available at the Air Center.  North of the main helibase, across the taxi way, is another field designated as a landing area for Type I or Type II helicopters.  Vehicle parking is available in the parking areas leading into and behind the Air Center building.  Idaho County Airport services include Jet A and 100LL, fuel servicing vehicles, and credit card pumps.  A map of the the Air Center and Idaho County Airport is in appendix J.

# The second operating base is located at the Musselshell Work Center on the Clearwater National Forest 14 miles east of Pierce, ID.  Additional district fire personnel are also stationed at the work center. Grass pads are located in the meadow across the road from the Musselshell Work Center.  Fire extinguishers and crash rescue kits will be staged at the helibase entrance.  Housing, laundry and cooking facilities are available for personnel stationed at the work center. Jet-A fuel is available in Lewiston which is approximatley 2 hours from the helibase.

# TRAINING

Training of the Clearwater / Nez Perce helicopter modules is the responsibility of the Helitack Supervisors. Training will include, but not be limited to, requirements set forth in the Interagency Helicopter Operations Guide and 5109.17 Chapter 40. The Helitack Supervisors, Assistant Helitack Supervisors, and Helitack Squad Leaders will assist in instructing  Zone and Regional helicopter training sessions.  Helicopter personnel will participate in daily physical fitness training.

The Helicopter Supervisors and Assistants, must complete helibase manager training, S-371.  All Zone helicopter managers are required to attend a regional helicopter managers workshop biannually.

# Position task books will be initiated by Unit Managers after the employee has completed prerequisite training for a position.  Zone Personnel desiring to develop aviation qualifications such as helicopter crewmember or manager positions are invited to detail to either module to develop or maintain qualifications.  Details must be approved through the employee’s direct supervisor and district ranger.  Helicopter personnel are available to assist Zone personnel in developing training plans to achieve their qualification goals.

# LOST OR OVERDUE AIRCRAFT

In the event that a Forest Service owned, leased or contracted aircraft is determined to be overdue (30 minutes after ETA at destination or if two successive periodic checks are not made) the dispatcher will immediately start a preliminary communications search by radio and telephone. All aircraft parking areas, ramps, hangars, terminals and intermediate stops should be checked.

When the aircraft is 30 minutes overdue and the preliminary search has not located the aircraft, proceed to the Northern Region Aircraft Crash, Search and Rescue guide overdue aircraft section.

If you are certain you have an aircraft accident, the first consideration must be the rescue and assistance of personnel involved in order to minimize injuries or fatalities. Start with the Aircraft Crash, Search and Rescue Guide - Downed Aircraft Section. Any Forest Service employee who knows or suspects an aircraft is down should call the Grangeville Interagency Dispatch Center. If the aircraft is not on a Forest Service mission,  Grangeville Interagency Dispatch will notify the proper authorities.

# SAFETY RESPONSIBILITY

Every employee has the responsibility of adhering to all safety requirements and to establish a safe working environment.  Periodic review of safety plans and sources of safety information should be done to    maintain currency and update of policy changes or additions.  This plan should be used as a guideline and is not intended to establish new policy, only to reinforce agency policy or standard operating procedure.

Safety principles have been reviewed here to emphasize their importance.  Deviation from policy or procedure could result in an accident or fatality.  Your first concern in air operations should be the safety of all personnel involved.

In addition to this plan, the Zone Air Operations plan, specific project plans and job hazard analysis' need to be reviewed by all persons working in air operations.

# HELICOPTER OPERATIONS CRASH RESCUE PLAN

# Purpose

The Grangeville/Musselshell helibases as well as other temporary helibases located on the Zone experience considerable use by the contract helicopter(s) based here from June thru September. Takeoffs and landings occur many times daily and assignments vary from personnel and internal cargo transport to external load operations including hover and remote hookups and aerial retardant delivery.

Since a majority of helicopter accidents occur on takeoffs and landings the potential for a major helicopter accident should not be ignored.  Proper planning and action could greatly reduce the severity and consequences of such an accident.

# Equipment

Equipment available in the event of a helicopter crash will vary dependant on location. A crash rescue kit as well as one or more 20 lb fire extinguishers are likely to be the only emergency equipment available at some sites. A Tri-Max 30® gallon Compressed Air / AFFF Foam Fire Extinguisher is located at the Grangeville Air Center and is available for use at temporary helibases.  Some sites such as Grangeville will have water with adequate hose to cover the heliport and a PA and loud speaker system for notification of ground personnel of an emergency.  In addition, Grangeville, Musselshell and most temporary helibases will have telephone and radio capabilities as well as personnel protective equipment and first aid kits that will be available.

# Roles and Responsibilities

Pilot:  Declares emergency to passengers, avoids ground personnel, fuel storage, etc., as

appropriate.

Helicopter manager:  Radios emergency and location to dispatch or helibase and performs in-flight emergency procedures.

# Passengers on board:  Keep calm and follow emergency flight procedures.

Helibase radio operator:  Declares emergency to ground personnel. Notifies dispatch immediately.

Identifies emergency landing area.  Identifies nearest medical facility.

Information to give:

1.	Declare emergency.

2.	Type of emergency.

3.	Location.

4.	Number of persons injured. (Do not give names over radio)

5.	Seriousness of injuries.

Also must monitor radio transmissions and coordinates rescue and support procedure outlined in this plan until relieved by the FMO, Assistant FMO or Helibase / Helicopter Manager .

FAO / Air Center Manager or Helibase / Helicopter  Manager:  (One person only will assume)  Coordinate the following as appropriate to the situation:

1.	Clear the landing area of personnel, fuel truck, etc.

2.	Designate personnel to operate the available emergency equipment.

3.	Designate person to call 911 and request fire department response, specify AFFF foam capabilities if available.

4.	Assure that ground personnel are fully Nomexed with gloves and protective helmet.

5.	Assign person to maintain and enforce 500 foot radius safety circle for unauthorized or unnecessary personnel.

Personnel at station:  The support personnel assigned will be exposed to the potential hazards of flying debris, rotor blades, explosions and fire.  Personal protection should be assured and excessive risks must not be taken.  Assembly point will be the air or communication center where ground personnel will immediately dress in protective clothing to support and operate assigned emergency equipment.  A minimum of five support personnel will be needed to accomplish necessary equipment operation as follows:

1.	One person operate extinguisher.

2.	Two people operate evacuation-rescue kit.

3.	One person operate 1 1/2" pump/hose located north of pad (at Grangeville).

4.	One person for personnel control.

# Other Additional Needs If Necessary:

1.	Personnel to operate additional fire extinguishers.

2.	Personnel to assist in extraction of aircraft occupants.

Rescue and first aid procedure:  The most immediate concern following a helicopter crash is fire.  Quick response and action is vital.  Personnel operating fire extinguishers should be the first rescuers on the scene to prevent fire or to extinguish fire before it builds.  They must also protect other rescuers and aircraft occupants.

The next step would be to evacuate aircraft occupants.  Personnel responsible should be aware of fire threat and act accordingly.  If fire exists or threat is great, no time should be taken to assess passenger condition, evacuation should be immediate.  If fire threat is not great, utmost care should be taken in evacuation of any injured occupants.  EMT's may be needed to assist if available.

Fire hose and water supply may be available for structure and vehicle fire protection.  Water should not be used as a primary means to control a fuel fire, unless equipped with appropriate foam application devices, and used only as a last resort.  Personnel operating fire hoses should be prepared to backup extinguisher personnel.

Crowd control must be accomplished to assure rescue personnel an adequate working environment and to guard others from hazards.  The person responsible should seek assistance, if needed, to accomplish this task.

If a first aid station is necessary, it should be located an adequate distance from crash site to eliminate hazards.  Staffing of the first aid station should be with qualified personnel.

When additional fire extinguishers are needed, personnel assigned will act as backup and position themselves to assist the personnel with primary fire suppression responsibility.

# Assignment

Due to the nature of work performed, training and availability, assignments for the emergency plan will be in groups. Helicopter personnel will have primary responsibility for implementation of this plan.  The persons responding first will assume responsibility of the most essential area that they are assigned until personnel needs are fulfilled.

# Training

Training will include the following:

1.	Review of this plan.

2.	Equipment familiarization and emergency flight procedures will be included in annual helicopter training.

3.	Mock drill at least once a season.

# Crash Near Grangeville/Musselshell

If a crash occurs near Grangeville/Musselshell and is immediately accessible, fire extinguishers and evacuation equipment will be transported to the crash site.  If crash site is not immediately accessible, the Forest Search and Rescue Plan will be implemented.

# Summary

Rescue operations should never contribute to or compound the problem that already exists.  If a helicopter crash should occur, remember that fire is a very likely result.  Immediate action is required.  Use only the number of people actually needed to control the situation.  Excess people only adds to the confusion.  Know and understand your role, equipment assignment and technique for use.

# ASSIGNMENTS FOR CRASH RESCUE PLAN

AND

FIRST AID PROCEDURE

# Priority #1: Rescue coordinators:  (only one will assume)

FAO / Air Center Manager

Helicopter Manager

Helibase Manager

Smokejumper OPS.

Priority #2: Fire extinguisher and/or Tri-Max® manning:

Any of the above plus:

# One (1) helicopter / aircenter personnel

Priority #3: Rescue and evacuation kit manning, Fuel and battery shutoff:

# Two (2) helicopter / aircenter personnel

Priority #4: Fire hose manning:

# One (1) helicopter / aircenter personnel

# Priority #5:Crowd control:

Any of the above or:

# One (1) helicopter / aircenter personnel

# Priority #6: First aid station manning:  (as needed)

E.M.T.     Any qualified personnel

# Priority #7: Additional fire extinguisher manning:  (as needed)

# Same assignments as Priority #2

Note:  Personnel to fill all priority positions may not be available.  Available personnel will fill positions in priority order.

All helicopter personnel will be trained in rescue and first aid procedures at initial employment and biannually thereafter.

# Appendix A

# Communications

# Phone Numbers

Radio Frequencies

See Attached Map for Boundaries

|  | WEST IA ZONE |  | NORTH LOW IA ZONE |
| --- | --- | --- | --- |
|  | EAST IA ZONE |  | NORTH HIGH IA ZONE |

| WEST IA ZONE |
| --- |
|  | RX | TX |  |  |  |  |  |
|  | NEZ WEST | FS Only 164.1375 | FS Only 169.1250 | Slate Pt. * 110.9(15) | HiCamp * 123.0(18) | Blk Butte * 131.8(20) | Hvns Gate * 136.5(21) | Cold Sprgs + 146.2(23) |
|  | PAF West | FS Only 171.5500 | FS Only 172.3500 | HrhyPoint156.7(25) |
|  | W-W | 166.0000 | 164.0250 | Somers Pt. 167.9(27) |
| IDL | Cotton Wood | 159.4650 Tone 136.500 | 151..2650 Tone 151.2650 |
|  | Jim Creek | 159.2325 Tone 131.8(20) | 151.3325 Tone 123.0(18) |
|  | Teaken | 159.3000 Tone 123.0(18) | 151.3250 Tone 100.0(12) |
|  | Woodrat | 159.4500 Tone 136.5(21) | 151.3100 Tone 100.0(12) |
| IDL | Air-Ground 1 | 151.1450 Tone 100.0(12) | 151.1450 Tone 100.0(12) | PRIMARY A-G |
|  |  | MISC | FREQS |  |
|  |  | RX | TX |  |
|  | Flight Following | 168.650 | 168.650 | National Flight Following |
|  | Air Guard | 168.6250 | 168.6250 | TX Tone 110.9 (15) |
| 1 | COM Use | 163.7125 | 163.7125 | Primary National G-G |
| 2 | COM Use | 168.6125 | 168.6125 | Second National G-G |
| W Band | IDL DIR 2 | 159.285 | 159.285 | IDL Statewide Tactical 77.0 Tone on RX/TX |
|  | Smkjmpr A-G | 168.550 | 168.550 | National Smkjmpr A-G |

| NORTH HIGH IA ZONE |
| --- |
|  | RX | TX |  |  |  |  |
|  | CWF | FS Only 171.5750 | FS Only 172.3750 | Beaver 123.0 (18) | Bear 136.5 (21) | Diablo 131.8 (20) | Rcky Rdg 146.2 (23) |
|  | CWF | FS Only 170.5000 | FS Only 172.2250 | Osier 123.0 (18) | Jnctn Mtn 167.9 (27) | Eagle 103.5(13) | Hemlock North 131.8 (20) |
|  | CWF | FS Only 173.7625 | FS Only 166.5625 | Castle Butte 136.5 (21) |  |  |  |
|  | C-NAir Ground | 164.8625 | 164.8625 | PRIMARY A-G |

| NORTH LOW IA ZONE |
| --- |
|  | RX | TX |  |  |  |  |
|  | CWF | FS Only 173.7625 | FS Only 166.5625 | Hemlock South 123.0(18) | Coolwater 131.8 (20) | Castle Butte 136.5 (21) | Doty Ridge 146.2 (23) |
|  | CWF | FS Only 170.5000 | FS Only 172.2250 | Eagle Pt. 103.5 (13) |
| IDL | Woodrat | 159.4500 Tone 136.5(21) | 151.3100 Tone 100.0(12) |
|  | Teaken | 159.3000 Tone 123.0(18) | 151.3250 Tone 100.0(12) |
|  | Elk Butte | 159.2550 Tone 100.0 (12) | 151.1750 Tone 123.0 (18) |
| WIDE Band | CPTPA 1 | 159.2700 | 151.2050 | Elk Butte TX Tn 127.3(19)WIDE Band |
| IDL | Air-Ground 1 | 151.1450 Tone 100.0(12) | 151.1450 Tone 100.0(12) | PRIMARY A-G |
| NPF REPEATERS ONLY |
| * | Repeaters operational |
| + | Operational June 2006 |
| ++ | Operational Aug 2006 |
| +++ | Operational Sept 2006 |

| EAST IA ZONE |
| --- |
|  | RX | TX |  |  |  |  |  |  |  |
|  | NPF | FS Only 168.6750 | FS Only 169.9500 | Iron * 110.9 (15) | Anderson Butte ++ 123.0 (18) | Burnt Knob +++ 131.8 (20) | Oregon Butte ++ 136.5 (21) | Fog Mtn * 146.2 (23) | Shissler + 156.7 (25) | Gardiner +++ 103.5 (13) |
|  | CWF | FS Only 173.7625 | FS Only 166.5625 | Coolwater 131.8(20) |
|  | CWF | FS Only 171.5750 | FS Only 172.3750 | Diablo 131.8 (20) |
|  | C-NAir Ground | 164.8625 | 164.8625 | PRIMARY A-G |

The FAA has issued a national transponder code 1255 for firefighting aircraft.  This code may be used by aircraft that are not in contact with air traffic control.  1255 can be utilized by all firefighting agencies, both federal and state when aircraft are engaged in firefighting operations.  								Tones #’s are specific to Technosonic Radios ONLY

Clearwater/Nez Perce Zone

Fire and Aviation Phone List

# Grangeville Interagency Dispatch Center:

Zone Coordinator, Dennis Crew		208-983-6801

Assistant Zone Coordinator, Operations

Rick Parker		208-983-6810

Assistant Zone Coordinator, Logistics

Julie Lombardo		208-983-6802

Aircraft Dispatcher, Linda Laing		208-983-6803

Dispatcher, Trisha Skinner		208-983-6813

Fax		208-983-4065

Grangeville Air Center		208-983-1964

Fax		208-983-9587

Helicopter Ops Fax		208-983-9580

Zone Aviation Officer, Willy Acton		208-983-9571

208-507-0942 CELL

Helitack Supervisor,  Nate Raff		208-926-6427

Home		208-926-7640

Helitack  Supervisor, Jeff Polack		208-983-9575

Home		208-983-0415

Contracting Officer, Kathy Benson		406-329-3525

Nez Perce N.F. Supervisors Office		208-983-1950

Clearwater N.F. Supervisors Office		208-476-4541

# Nez Perce N.F.  Ranger Districts:

Slate Creek RD    FMO Kevin Chaffee		208-839-2211

"        "   After hours #		208-839-2335

Seed Orchard Helibase		208-628-3130

Clearwater RD     FMO  Barry Ruklic		208-983-4032

"           After hours #		208-935-7928

Moose Creek RD  FMO Erin Law 		208-926-4258

"         " After hours #		208-926-7969

Red River RD        FMO  Tim Button		208-842-2124

"        "      After hours #		208-842-2155

Dixie Guard Station		208-842-2237

Dixie Air Ops Trailer		208-842-2236

Mullins Airstrip		208-842-2671

# Clearwater N.F.  Ranger Districts:

North Fork RD   FMO Mike Lubke		208-476-4541

Canyon WC    		208-476-8306

Kelly Forks WC		208-476-8304

Pierce WC		208-464-2573

Lochsa RD         FMO  Chris Gauthier		208-926-6419

Kamiah RS		208-935-2513

Musselshell WC		208-435-9326   Fax  4636

Powell RS             FMO Mark Wilson		208-942-0345

Palouse RD          FMO  Tom McWilliams		208-875-1131

# Jet A Vendors:

Idaho County Airport  (Grangeville)               	208-983-1565

Minuteman Aviation (Missoula, Mt.)             	406-728-9363

Hamilton Aviation   (Hamilton, Mt.)                 	406-363-3833

Stout Flying Service  (Lewiston, Id.)  		208-743-8408

# Regional Phone List

Regional Aviation Officer – Rick Hafenfeld		406-329-4903

Cell Phone        			406-370-3340

Helicopter Operations Specialist - Bob Quirino		406-329-4915

Cell Phone			406-370-3343

Aviation Safety Manager – Eddie Morris		406-329-4918

Cell Phone			406-370-3341

Helicopter Inspector Pilot - Tim Pfahler		406-329-4984

Cell Phone                                      			406-370-3342

A/C Maintenance/Safety Inspector - Jeff Holwick		406-329-3120

Cell Phone			406-544-4072

A/C Contacting Officer - Kathy Benson		406-329-3525

LEI  Regional Special Agent  -  Roger Seewald		406-329-3590

National Contracting Officer – Frank Gomez		208-387-5347

NRCC Flight Following  (Missoula) 			800-247-8328

NICC Flight Following  (Boise)			800-994-6312

# Local Lodging Facilities

| GRANGEVILLE |  |  |
| --- | --- | --- |
| Monty's Motel | 700 W. Main, Grangeville | (208) 983-2500 |
| Elkhorn Lodge | South 1st and E, Grangeville | (208) 983-1500 |
| Downtowner Inn | 113 E. North, Grangeville | (208) 983-1110 |
| Super 8 Motel | 801 W.S. 1st St. Grangeville | (208) 983-1002 |
| WHITEBIRD |  |  |
| Hoots Motel | Highway 95 South, Whitebird | (208) 839-2265 |
| Whitebird Motel | Whitebird | (208) 839-2308 |
| RIGGINS |  |  |
| Riverview Motel | 704 Main, Riggins | (208) 628-3041 |
| Salmon River | 1203 S. Hwy 95, Riggins | (888) 628-3025 |
| Bruce Motel | 515 Main, Riggins | (208) 628-3005 |
| Best Western Salmon Rapids | US Hwy 95 | (208) 628-2743 |
| Riggins Motel | 615 S. Main | (800) 669-6739 |
| LUCILE |  |  |
| Steelhead Inn | Milepost 210 Hwy 95, Lucile | (208) 628-3044 |
| COTTONWOOD |  |  |
| The Country Haus | 407 Foster, Cottonwood | (208) 962-3391 |
| DIXIE |  |  |
| Silver Spur Lodge | Main St. Dixie | (208) 842-2417 |
| Southern Star Inn | Comstock Road, Dixie | (208) 842-2730 |
| POWELL |  |  |
| Lochsa Lodge | Powell | (208) 942-3405 |
| PIERCE |  |  |
| Pierce Motel | 509 S. Main, Pierce | (208) 464-2324 |
| The Timber Inn | 2 S. Main, Pierce | (208) 464-2736 |
| Clearwater Hotel & Café | 110 S. Main, Pierce | (208) 464-2721 |
| LOWELL |  |  |
| Lowell Motel & Gas | Lowell | (208) 9268822 |
| Three Rivers Resort | Lowell | (208) 926-4430 |
| Ryan’s Wilderness Inn & Cafe | Highway 12, Lowell | (208) 926-4706 |
| KAMIAH |  |  |
| Clearwater 12 Motel | Highway 12, Kamiah | (208) 935-2671 |
| Sundown | 1004 3rd St. Hwy 12, Kamiah | (208) 935-2568 |
| Lewis & Clark Resort | Hwy 12, S of Kamiah | (208) 935-2556 |

|  | LOCAL EATING FACILITIES |  |
| --- | --- | --- |
| GRANGEVILLE |  |  |
| Barb’s | 123 W. Main, Grangeville | (208) 983-1019 |
| The Depot | Highway 95 North, Grangeville | (208) 983-0176 |
| Hilltop | 500 E. Main | (208) 983-1714 |
| Hong Fa | 521 W. Main, Grangeville | (208) 983-1701 |
| Palenque Mexican Restaurant | 711 W. Main, Grangeville | (208) 983-1335 |
| Pizza Factory | 126 W. Main, Grangeville | (208) 983-5555 |
| Oscar’s Restaurant | 101 E. Main, Grangeville | (208) 983-2106 |
| Subway | 179 Greenacres Lane | (208) 983-3054 |
| The Shanghai Restaurant | 124 W. Main, Grangeville | (208) 983-0485 |
| Taco Bell | Main and Highway 95, Grangeville | (208) 983-7508 |
| Ernies Steakhouse | 622 W. Main, Grangeville | (208) 983-2220 |
| WHITEBIRD |  |  |
| Hoots Café | Hwy 95, Whitebird | (208) 839-2265 |
| Silver Dollar | Main St., Whitebird | (208) 839-2293 |
| RIGGINS |  |  |
| Back Eddy Grill | 533 N. Main, Riggins | (208) 628-9233 |
| Summersville Café | 106 S. Main, Riggins | (208) 628-3211 |
| Salmon River Inn | 129 S. Main, Riggins | (208) 628-3813 |
| Cattlemens | 601 S. Main, Riggins | (208) 628-3195 |
| Seven Devils Steakhouse | 312 N. Main, Riggins | (208) 628-3351 |
| Way Back Steakhouse | Rodeo Club 208 S. Main, Riggins | (208) 628-9260 |
| PIERCE |  |  |
| Cedar Inn Restaurant & Lounge | 412 S/ Main, Pierce | (208) 464-2704 |
| Wink & Smile | 703 S. Main, Pierce | (208) 464-2681 |
| KAMIAH |  |  |
| Palenque Mexican Rextaurant | 501 4th St. , Kamiah | (208) 935-7700 |
| Sacajawea Café | Lewis-Clark RV Park, Kamiah | (208) 935-1958 |
| The Hub | 406 Main, Kamiah | (208) 935-1670 |

# Appendix B

# Helispots

The following is a listing of several helispots on each district.  It is by no means comprehensive. Lat/Longs are in degrees, minutes, and 100ths of minutes, NOT seconds.  All helispots and landing areas should be thoroughly sized up by the pilot and helicopter manager prior to use to ensure conditions at the site allow a safe landing or take-off.  Feedback to the Helicopter Program Manager or Helitack Managers  from pilots or managers concerning the condition of helispots is appreciated.

|  |  | HELISPOTS |  | YEAR |
| --- | --- | --- | --- | --- |
|  |  |  |  |  | LAST |
| NAME | ELEV. | LAT. | LONG. | NOTES | USED |
| NEZ PERCE N.F. |  |  |  |  |  |
| Grangeville Air Center (S80) | 3309 | 45 56.3 | 116 07.8 | 2 Pads, Jet A |  |
| Salmon River District (D-1) |  |  |  |  |  |
| Allison Creek | 1850 | 45 25.2 | 116 09.3 |  | 2003 |
| Chair Point | 6951 | 45 28.8 | 116.13.1 | Guy Wires, Type III | 2001? |
| East Graves Point | 5200 | 45 38.37 | 116 22.60 | IGE, Type III | 1997 |
| Florence Helibase | 6240 | 45 31.35 | 115 59.97 | Multiple pads | 2003 |
| Green Acres | 7440 | 45 20.6 | 116 29.9 | IGE, Type III | 2002 |
| Heaven's Gate Lookout | 8429 | 45 22.7 | 116 29.1 |  | 2005 |
| Island Bar | 1750 | 45 25.3 | 116 16.8 | Type I, IGE, Public | 1994 |
| Rapid River Fish Hatchery | 2150 | 45 21.3 | 116 23.4 | Wires, Permission, Type III | 2000 |
| Seed Orchard Helibase | 1800 | 45 34.56 | 116 18.04 | Wires, windsock, pad | 2005 |
| Shorts Bar Public Beach | 1781 | 45 24.85 | 116 18.00 | Type I, IGE, Public | 1994 |
| Slate Creek Airstrip 1S7 | 1660 | 45 40.7 | 116 17.9 | Wire windsock | 2002 |
| White Bird Ridge | 5108 | 45 18.81 | 116 24.18 | IGE, Type II, 4WD Road | 1999? |
| Wyant Bridge | 3400 | 45 16.64 | 116 25.42 | Type III, Bench | 2004 |
| Clearwater District (D-4) |  |  |  |  |  |
| Hungry Ridge | 4600 | 45 48.5 | 115 55.6 |  | 2004 |
| McComas Meadows | 3200 | 45 53.4 | 115 55.4 | Near Bridge | 1998 |
| Mill Creek Meadow | 4600 | 45 42.4 | 116 01.8 | OGE | 2002 |
| Pilot Knob Lookout | 7135 | 45 54.6 | 115 42.8 |  |  |
| Ralph Smith Place | 3600 | 45 50.1 | 115 52.3 | Type I, IGE | 2003 |
| W. Fork Clear Creek Pit | 3250 | 46 01.6 | 115 49.5 | Type II, OGE | 2002 |
| Elk City District (D-5/8) |  |  |  |  |  |
| Boston Mountain | 7648 | 45 38.9 | 115 11.1 | Wilderness Boundary | 2004 |
| Cape Horn | 6140 | 45 30.85 | 115 35.46 | Type 3, two way, HIGE | 2006 |
| Concord Airstrip | 7655 | 45 35.4 | 115 40.8 | Private Property | 2005 |
| Dixie FS Airstrip A05 | 5148 | 45 31.4 | 115 31.3 | Windsocks | 2003 |
| Elk City Airstrip S90 | 4097 | 45 49.4 | 115 26.3 | Windsock | 2003 |
| Green Mountain Lookout | 7227 | 45 46.3 | 115 04.5 | Type III, Road | 2003 |
| Mackay Bar Airstrip | 2172 | 45 22.7 | 115 30.1 | Private Property, FEES |  |
| Mullins Airstrip BCS | 4299 | 45 43.3 | 115 22.2 | Windsock | 2004 |
| Oregon Butte Lookout | 8465 | 45 31.4 | 115 39.9 | Type III, OGE | 2005 |
| Rabbit Point | 6400 | 45 30.0 | 115 28.5 | Type II, Gunsight | 2003 |
| Sheep Hill Lookout | 8405 | 45 35.4 | 115 04.9 | Wilderness | 2004 |
| Shepp Ranch Airstrip | 2100 | 45 26.3 | 115 39.9 | Private | 2005 |
| Whitewater | 4500 | 45 32.00 | 115 20.00 | Type 3 HIGE, two way | 2006 |
| Moose Creek District (D6) |  |  |  |  |  |
| Buck Meadows | 5700 | 45 59.4 | 115 25.9 | Type III | 2005 |
| Cedar Flats | 1522 | 46 05.7 | 115 32.2 | Windsock, Type II | 2005 |
| Coolwater Lookout | 6929 | 46 09.4 | 115 27.8 | Type III | 2003 |
| Disgrace Butte | 6584 | 45 54.80 | 115 09.88 | Type III | 2004 |
| Gardiner Lookout | 6597 | 45 58.1 | 114 45.3 | Type III, Wilderness | 2001 |
| Horse Creek Confluence | 4200 | 45 59.39 | 115 20.01 | Type III | 2005 |
|  |  | HELISPOTS |  | YEAR |
|  |  |  |  |  | LAST |
| NAME | ELEV. | LAT. | LONG. | NOTES | USED |
| NEZ PERCE N.F. |  |  |  |  |  |
| Moose Creek District (D-6) |  |  |  |  |  |
| Horse Ridge | 5650 | 45 58.25 | 115 20.78 | Type III, Meadow | 1999 |
| Indian Hill Lookout | 6816 | 45 59.8 | 115 14.1 | Type III | 2003 |
| Johnson Bar | 1500 | 46 06.23 | 115 33.52 | Type I, Campground | 1996? |
| Meadow Creek Cabin | 3050 | 45 52.96 | 115 14.22 | Type III | 2005 |
| Moose Creek Airstrip 1U1 | 2454 | 46 07.7 | 114 55.3 | Windsock | 2004 |
| Moose Creek Ranch Airstrip | 2300 | 46 10.53 | 114 53.24 | Wilderness | 1997 |
| Racetrack | 1780 | 46 02.4 | 115 17.8 | Type I, Narrow Road | 2005 |
| Shearer Airstrip 2U5 | 2634 | 45 59.8 | 114 50.3 | Windsock | 2003 |
| Shissler Lookout | 5375 | 46 10.3 | 114 56.5 | Type III, Wilderness | 2004 |
| CLEARWATER N.F. |  |  |  |  |  |
| Pierce/Lochsa District |  |  |  |  |  |
| Boulder Flats | 2091 | 46 20.0 | 115 19.0 | Type II | 2004 |
| Doris Butte | 4753 | 46 34.15 | 115 25.19 | Type III, Knob | 2005 |
| Fidelity Gulch Pit | 3900 | 46 31.1 | 115 40.3 | Type II |  |
| Gold Dollar Flats | 3087 | 46 27.55 | 115 46.65 | Type II, Meadow |  |
| Hemlock Butte Lookout | 6053 | 46 28.6 | 115 37.3 |  |  |
| Kamiah Airstrip S73 | 1194 | 46 13.16 | 116 00.81 | Windsock | 2003 |
| Kooskia Airstrip S82 | 1265 | 46 08.0 | 115 58.9 | Windsock | 2004 |
| Little Weitas Butte | 5900 | 46 27.37 | 115 25.23 | Type III, 1 Mile North | 2004 |
| Mex Mountain Work Center | 5050 | 46 19.4 | 115 35.7 | OGE, 2 pads | 2005 |
| Monroe Butte | 6400 | 46 32.95 | 115 13.25 | Type II, North | 2002 |
| Musselshell Work Center | 3700 | 46 21.43 | 115 44.56 | Type II | 2005 |
| Nineteen Mile Camp | 4500 | 46 29.76 | 115 30.74 | Type II, Ridgetop meadow | 2003 |
| Obia Cabin | 2800 | 46 21.46 | 115 23.77 | Type III, Ridge above cabin | 2005 |
| Smith Creek | 2000 | 46 10.00 | 115 44.05 | Type III, Road | 2004 |
| Walde Lookout | 5221 | 46 14.74 | 115 38.07 | Type III | 2003 |
| Weitas Butte Lookout | 5967 | 46 33.8 | 115 26.4 | Type III | 2004 |
| Weitas Meadows | 5400 | 46 26.02 | 115 29.03 | Type II, Meadow | 2002 |
| Windy Creek |  | 46 29.6 | 115 28.5 | Type III | 2004 |
| Palouse District |  |  |  |  |  |
| Cedar Grove Camp | 2800 | 47 01.438 | 116 41.908 | Type II, OGE | 1998 |
| Potlatch | 2500 | 46 55.6 | 116 54.7 | Type I, IGE | 2002? |
| White Pine Creek | 2900 | 47 01.908 | 116 43.113 | Type III, OGE | 1998 |
| North Fork District |  |  |  |  |  |
| 4th of July Bridge |  | 46 40.04 | 115 22.73 | Type II, Bridge | 1999 |
| Black Mountain Lookout | 7077 | 46 52.73 | 115 33.12 | Type III, OGE | 2005 |
| Canyon Work Center | 1747 | 46 50.2 | 115 35.21 | Windsock, Jet A | 2005 |
| Cayuse Airstrip S74 | 3700 | 46 40.0 | 115 04.3 | Windsock | 2000 |
| Clearwater Valley Hospital | 1025 | 46 29.5 | 116 15.3 | Concrete Pad | 1999 |
|  |  | HELISPOTS |  | YEAR |
|  |  |  |  |  | LAST |
| NAME | ELEV. | LAT. | LONG. | NOTES | USED |
| CLEARWATER N.F. |  |  |  |  |  |
| Eagle Point | 5709 | 46 48.02 | 115 32.13 | Type III, OGE | 2003 |
| Elmer Creek | 4550 | 46 55.45 | 115 37.07 | Type III | 1996 |
| North Fork District |  |  |  |  |  |
| Hanson Meadows | 3500 | 46 41.9 | 114 55.2 | Type III | 1996 |
| Isabella Landing | 2000 | 46 53.49 | 115 35.47 | Type I | 2000 |
| Junction Lookout | 6457 | 46 41.6 | 115 16.7 | Type III, OGE | 2004 |
| Kelly Creek Work Center | 2737 | 46 43.13 | 115 15.65 | Windsock, Type II, IGE | 2004 |
| Mallard Lake | 6400 | 46 55.61 | 115 30.63 | Type II, Meadow by lake | 1999 |
| Never Again Flats | 3800 | 46 39.08 | 115 06.85 | Type II, Meadows | 2000 |
| Old Bungalow | 2300 | 46 38.0 | 115 30.5 | Type II, above river | 1999 |
| Old Kelly Creek | 3000 | 46 43.3 | 115 16.7 | Type III | 1998 |
| Orofino Airstrip S68 | 1005 | 46 29.48 | 116 16.61 | Windsock | 2005 |
| Osier Ridge Lookout | 6115 | 46 49.7 | 115 00.9 | Type III | 2003 |
| Powell District |  |  |  |  |  |
| Bear Mountain Lookout | 7184 | 46 25.9 | 114 55.4 | Type III | 2003 |
| Beaver Ridge Lookout | 7370 | 46 34.9 | 114 26.4 | Type III | 2004 |
| Diablo Lookout | 7461 | 46 17.8 | 114 37.0 | Type III, Wilderness | 2002 |
| Elk Summit G.S. | 5756 | 46 19.8 | 114 39.0 | Type II, IGE | 1999 |
| Fish Lake Airstrip S92 | 5646 | 46 19.81 | 115 03.79 | Windsock | 2003 |
| Lolo Pass | 5235 | 46 37.75 | 114 32.2 | Parking Lot | 2003 |
| Lost Lakes Meadow | 6000 | 46 37.6 | 114 46.4 | Type III, IGE | 1999 |
| Plum Creek Pit | 3500 | 46 30.89 | 114 41.42 | 2 Pads, | 2004 |
| Post Office Gravel Pit | 2900 | 46 28.03 | 114 59.08 | Type III, OGE | 2005 |
| Powell R.S. | 3400 | 46 30.53 | 114 42.53 | 2 Pads, Jet A | 2005 |
| Saddle Camp Road | 2750 | 46 27.2 | 115 05.0 | Turnout off Hwy 12 | 1997 |

# Appendix C

# Sunrise / Sunset Charts

# Appendix D

# Clear/Nez Zone

Emergency Rescue Plan

CLEARWATER/NEZ PERCE ZONE

# EMERGENCY RESCUE PLAN

# MEDICAL FACILITIES

| MEDICAL FACILITY *********************** | LOCATION ************** | LATITUDE ********** | LONGITUDE *********** | CONTACT FREQ. *************** | REMARKS ***************** |
| --- | --- | --- | --- | --- | --- |
| SYRINGA GENERAL HOSPITAL | GRANGEVILLE 208-983-1700 | N 45 56.3 | W 116 07.8 | 155.340 88.5 | NO PAD Land at Airport (S80) |
| CLEARWATER VALLEY HOSPITAL | OROFINO 208-476-4555 | N 46 29.5 | W 116 15.3 | 155.340 | PAD for Type 3 |
| ST. MARY'S HOSPITAL | COTTONWOOD 208-962-3251 | N 46 03.2 | W 116 21.5 | 155.340 123.0 | PAD for Type 2 |
| ST. JOSEPH'S REGIONAL MEDICAL CENTER | LEWISTON 208-743-2511 | N 46 25.0 | W 117 01.3 | 155.340 141.3 | 9,000# Roof PAD |
| GRITMAN MEDICAL CENTER | MOSCOW 208-882-4511 | N 46 44.4 | W 117 01.2 | 155.340 None | NO PAD Land W Kibbie Dome |
| SACRED HEART MEDICAL CENTER | SPOKANE, WA 509-455-3131 | N 47 39.8 | W 117 24.0 | 155.340 | 10,000# Roof PAD MED-STAR |
| ST. PATRICK'S MEDICAL CENTER | MISSOULA, MT 406-543-7271 | N 46 52.524 | W 113 59.969 | 155.280 | Lifeflite on Pad Land with Permission |
| McCALL MEMORIAL HOSPITAL | McCALL 208-634-2221 | N 44 54.3 | W 116 06.3 | 155.280 155.340 (Primary) | Pad in Parking Lot Prior notification rqd. |

# HELICOPTER MED-EVAC EMS PROVIDERS

| LOCATION *************************** | AIRCRAFT TYPE ********************** | PHONE NUMBER ********************** | REMARKS *********************** |
| --- | --- | --- | --- |
| SPOKANE, WA MEDSTAR | EC-135 | 800-991-7363 | Sacred Heart and Deaconess |
| MISSOULA, MT LIFE FLIGHT | AS350 B3 | 800-991-7363 | St. Patrick's Medical Center |
| BOISE, ID LIFEFLITE | Bell-222 | 800-521-2444 | St. Alphonsus Hospital |
| Mc Call, Id. | Bell-206LIII | 800-521-2444 | St. Alphonsus Hospital |
| SPOKANE, WA. | UH1-N (212) | 800-851-3051 R.C.C. | Military, Hoist Capable |
| IDAHO FALLS, ID | AGUSTA 109 K-2 | 800-247-4324 | High Altitude Capable |

# OTHER CONTACTS

| IDAHO COUNTY SHERIFF |  |  | MONTANA |  |
| --- | --- | --- | --- | --- |
| GRANGEVILLE | 208-983-1100 |  |  |  |
| KOOSKIA/STITES | 208-926-4221 |  | RAVALLI COUNTY |  |
| EMERGENCY ONLY | 911 |  | SHERIFF HAMILTON | 406-363-3033 |
| CLEARWATER COUNTY SHERIFF |  |  | MINERAL COUNTY |  |
| OROFINO | 208-476-4521 |  | SHERIFF SUPERIOR | 406-822-4861 |
| EMERGENCY ONLY | 911 |  |  |  |
|  |  |  | IDAHO POISON CENTER | 1-800-860-0620 |
| LATAH COUNTY SHERIFF |  |  | IDAHO EMS 1 RADIO FREQ | 155.340 |
| MOSCOW | 208-882-8580 |  | IDAHO EMS 2 RADIO FREQ | 155.280 |
| EMERGENCY ONLY | 911 |  |  | REVISED 1/05 |

| MEDICAL SERVICES-HELICOPTER AMBULANCE REQUEST FORM |
| --- |
| Caution: EMS Helicopters Do Not Usually Carry Extrication Equipment or Personnel Trained In These Procedures; Ensure That This Capability is Ordered Through Local S&R. |
| Date: |  |  | Time: |  |
| A. | ACCIDENT SCENARIO (How did the accident occur?) |  |
| B. | INJURY INFORMATION | Total number of personnel to be transported: |  |
| (If available, Supply Vital Signs, Type and Extent of Injury, Etc.) | AMBULATORY ? |
|  |  |  | YES/NO |
| PATIENT 1: |  |  |  |
| PATIENT 2: |  |  |  |
| PATIENT 3: |  |  |  |
| PATIENT 4: |  |  |  |
| C. | INCIDENT SITE INFORMATION: |
| 1. | Location of Accident: | Twn: |  | Rge: |  | Sect.: |  | 1/4 S: |  |
|  | Latitude: |  | Longitude: |  |
|  |  | NM | @ |  | Degrees | Off |  | Vor |
| 2. | Conditions At Scene: | Windspeed/Direction |  | Elev: |  | MSL |  |
|  |  | Temp: |  |
| 3. | Visibility and Sunset/Sunrise Limitations: |  |
| 4. | Terrain Factors: |  |
| 5. | Helispot Size and Condition | (Is It Completed Or When Will It Be): |  |
| 6. | Proximity of Helispot to Injury Site: |  |
| 7. | Special Information, Flight Haz. Etc.: |  |
| D. | CONTACT INFORMATION |
| 1. | Unit/Agency |  | 2. | Phone Number |  |
| 3. | Radio Frequency of Agency: | VHF-AM |  | VHF-FM |  |
| 4. | Ground Contact: |  |
|  | Radio Freq | Primary | VHF-AM |  | VHF-FM |  |
|  | At Accident Site |  |  |
|  | Ground Contact: |  |
|  | Radio Freq | Secondary | VHF-AM |  | VHF-FM |  |
| 5. | Other Aircraft In Area (Call Signs): |  |
|  | Radio Freq | Primary | VHF-AM |  | VHF-FM |  |
|  | Of Other Aircraft |  |  |  |
|  | Air to Air Contact: |  |
|  | Radio Freq | Secondary | VHF-AM |  | VHF-FM |  |
| 6. | Jet A Fuel Available From What Location Nearest to Site: |  |

##### Appendix E

#### SAFECOM

Safecoms may be viewed through the Forest Service Aviation Management Web Page (www.aviation.fs.fed.us).  For assistance on submitting a Safecom, contact Willy Acton, Zone Aviation Officer, at (208) 983-9571 or send a hard copy of the Safecom to him, c/o Grangeville Air Center, Rt. 2 Box 475, Grangeville, ID   83530.  He can then gather info from all related parties prior to submission to the Database. SAFECOM’s shall be submitted to the Zone Aviation officer within 24 hours for review. A verbal notification is required as soon as practical.

# Appendix D

# Local Weather, Fire Behavior

& Environmental Considerations

Local Weather Conditions:  The winds for central Idaho are predominately from the southwest, with low level winds being upslope.  However, due to the varied topography of the area, local winds are often influenced by terrain and atmospheric instability.  Hot summer temperatures can produce significant convective activity.  Thundercells can and often develop in the afternoon and evening.  Winds near storms may be very strong and erratic.  Hail may be associated with these thunderstorms.

Temperatures on the  Clearwater and Nez Perce National Forests can vary widely.  Lows in the winter may drop to -30 degrees in the higher elevations, with summer highs in the lower river canyons exceeding 105 degrees.  Elevations range from 1000 feet at Orofino and Hells Canyon to over 8500 on the Bitterroot divide, 8938 at Buffalo Hump and 9393 in the Seven Devils.  In the higher elevations, it is possible to have snowfall during any month of the year, and nights are generally quite cool.   Due to temperature and elevation extremes,  Pilots and Helicopter Managers must constantly be aware of actual conditions at the site, and plan accordingly.

Fire Behavior:  Due to the large area covered by the Clearwater/Nez Perce Fire Zone, local fuels can vary widely.  Fuel Model 2,  in the grass  group, can be found along the lower elevations of the Salmon and Snake Rivers, with Fuel Mod el 8 and 10, in the timber litter group, being quite common on most of the zone.  Fuel Model 11, 12, and 13, in the slash group,  can be found in areas where there has been logging activity.  Some areas that were burned over years ago may have some of the shrub group fuel models.  Descriptions of the fuel models can be found in Appendix B of the Fireline Handbook.

Fire behavior is often driven by weather conditions and slope.  Most of the Clearwater/Nez Perce Zone is characterized by extremely rugged terrain, where slope and aspect may contribute significantly to fire behavior.  Erratic winds are common in the hot summer months, especially near thunderstorm activity.  Local winds are often influenced by convection and topography, and it is not uncommon for winds to switch 180 degrees daily.

Spring is usually very moist, with several inches of rainfall normal in May and June.  However, by July and August, it is common to have very little rain for extended periods.  Thunderstorms ignite most of the fires, and holdover fires resulting from wet thunderstorms are common for weeks following the storm.  Person-caused fires are not common, but usually will occur on dry years after the start of hunting season.  September usually brings cooler temperatures and an increase in moisture, but the weather may often remain hot and dry into October.  Fire season usually peaks in mid-August, but will usually not end until there is significant snow on the higher elevations.  The zone averages 400 fires annually.

Environmental Considerations:  Over half of the Clearwater / Nez Perce Zone is wilderness, proposed wilderness, or roadless areas.  Most of our waterways contain anadromous fish or other threatened and endangered species.  Wolves have been reintroduced to Central Idaho and can be found on both forests.  Noxious weeds are becoming more of a problem.  For these and other reasons, there are many environmental considerations that need to be addressed while operating on the Zone.  Fueling will usually be done 300 feet or more from running streams, and fuel containment systems may need to be set up at some sensitive sites.   Minimum impact suppression tactics (MIST) should be adhered to whenever possible in constructing helispots, fireline, camping areas, etc. anywhere on the zone, both in and out of the wilderness.  Landings in wilderness must be pre-approved, as does the emergency use of motorized equipment.  Care should be taken to help limit the spread of noxious weeds by avoiding infested areas if possible, and inspecting vehicles, cargo nets, packs, clothing, etc. for weed seeds.

See also following page, Aquatic Programmatic Mitigation Measures for Fire Management

Aquatic Programmatic Mitigation Measures for Fire Management

June 1999

# FIRELINE CONSTRUCTION:

*	Firelines will be constructed to minimize water concentration, install

waterbars concurrent with line construction.

*	Do not use stream bottoms as constructed or improved fireline.

*	Any machine fireline needs to be reviewed by Aquatics Specialist before

construction.

*	Firelines on extended attack and project fires must be reviewed by Resource

Advisor for possible rehabilitation needs.

# WATER DRAFTING

*	Review map and criteria of adult staging and spawning areas for  sensitive

streams  near fire location.

*	Use fuel containment system for all portable pump operations.

*	Minimize risk of accidental fuel spillage into live water.

*	Chemical injection system will only be installed on the discharge side of the

pump.

*	All intakes for portable pumps will be equipped with screens.

*	Do not backflush pumps and hoses containing chemicals into streams or lakes.

*	Resource Advisor will review all sumps in sensitive streams for possible

rehabilitation needs.

# HELICOPTER BUCKET DIPPING/RETARDANT DROPPING

*	Review map and criteria of adult staging and spawning areas for  sensitive

streams  near fire location.

*	Review map of adult staging and spawning areas for  sensitive streams  near

fire location.

*	Avoid or minimize risk of delivery of foams, retardant, and surfactants to

surface waters.

*	No chemical injections system will be used on helicopter buckets,  disconnect,remove and rinse bucket clean if system is installed on bucket.

*	Drop retardant on ridges and side slopes, if dropping near streams, drop

retardant perpendicular to stream not parallel with  stream.

# CAMPS AND HELIBASES

*	Locate camps and helibases outside of RCHAs.

*	Historically used helibases and basecamps will be reviewed by ID Team

including aquatics specialist and camp layout and use conditions documented

and kept in FMP.

*	Resource Advisor will review new camps and helibases located in RHCAs for use

and rehabilitation requirements.

*	Hazardous fuel containment system will be used for repeated use fueling sites

in RHCAs,

*	Locate helicopter fueling sites outside of RHCAs.

# Appendix E

# Maps

All maps are vailable in the Pilot Briefing Package

Clearwater / Nez Perce Flight Hazard Map

Detection Flight Routes

Clearwater/Nez Perce Repeater Maps

Clearwater/Nez Perce Helicopter Program

Operating Plan for the 2006 Fire Season

Helitack personnel are assigned to the Clearwater Ranger District and the Lochsa Ranger District.  The following guidelines will be used for the 2006 Fire Season.

Helicopter Staffing

The Helitack Supervisors will be directly supervised by the DFMO’s who will be responsible for approving time and attendance reports, travel vouchers and leave.  The DFMO’s will also be responsible for advising the Helitack Supervisors of their job standards and will complete performance reviews .

Direct supervision of the aircraft contracts and modules will be conducted by the Helitack Supervisor or delegated by the Helitack to the core group of Helitack personnel or other qualified individuals at the discretion of the Helitack Supervisor.

Helicopter and Module Availability

The daily availability and staffing of the helicopter will be communicated to the District Duty Officer and the Grangeville Interagency Dispatch Center.  GVC will be notified thru the use of the Resource Status Report and morning phone call completed by the assigned district Duty Officer.

During times of low fire activity within the Fire Zone, core Helitack Module members will be available for off forest fire assignments to fill critical national aircraft management and incident aviation support roles.

The helicopter and module may be available for off zone assignment, if zone fire activity is low and the Zone Fire Staff, Aviation Officer and Center Manager concur on releasing the resource for any off forest assignments.

Helicopter Orders on Zone

All District Orders for helicopter missions will be processed thru GVC.  Some basic information should be included in the orders to enhance missions planning and safety.

State type of mission being requested:	Also include in the order:

Passenger transport 				Destination: Physical Name & Lat &Long

District Personnel IA				Request Date & ETA

Direct IA					Specialized Equipment Needs

Bucket Work					Communication Plan

Longline					Cargo Weight & Type

Recon						List of Hazardous Materials

S/R, Medi-Vac					Helicopter Type needed

Aerial Ignition:					Management Code

PSD					Passenger(s) Name(s) & Weight(s)

Helitorch

After Action Review of mission

AAR will be conducted with HEMG by District FMO or delegate (IC, Duty Officer).

For assignments of two or more days, District FMO or delegate will conduct AAR with HEMG and provide Crew and/or Individual Evaluation.

Hiring of Helitack Module Personnel

All hiring is done under the authority of the appropriate Line Officer in collaboration with the Zone Aviation Officer.

Helicopter Program Monitoring

A review of the overall program will be performed at the end of the fire season by the Zone Aviation Officer. The helicopter program and support will be subject to informal field reviews throught the season.

# Comments

Need to add full phone list

Need to add Musselshell helibase fax and phone #. Update Nates desk #

Need to add fax # for Jeff

# Text boxes

HelicopterCrewmember

GS-0462-4 Temp

Ryan Hickey

HelicopterCrewmember

GS-0462-4 Temp

Julie Christenson

Helicopter Crewmember

GS-0462-4 Temp

Bethany Anderson

Helitack Senior Firefighter

GS-0462-05 Temp

Jerry Mathes

Helitack Senior Firefighter

GS-0462-05 13/13

Jerod Kidd

Helitack Squad Leader

GS-0462-06 13/13

VACANT

Helitack Squad Leader

GS-0462-06 13/13

Doug Colaprete

Assitant Helitack Supervisor

GS-0462-08 18/8

Willie Allman

Helitack Supervisor

GS-0462-09 PFT

Nate Raff

Helicopter Crewmember

GS-0462-04 1039

Robert Feeley

Helicopter Crewmember

GS-0462-03 STEP

Brett Jensen

Helitack Senior Firefighter

GS-0462-05

Robert Giron

Robert Zielke

Helitack Senior Firefighter

GS-0462-05 13/13

Robert Zielke

Helitack Squad Leader

GS-0462-06 13/13

Jeremey Beeson

Helitack Squad Leader

GS-0462-06 13/13

Thomas Clay

Assitant Helitack Supervisor

GS-0462-08 18/8

Eric Gleckler

Helitack Supervisor

GS-0462-09 PFT

Jeff Polack

Clearwater RD FMO

Barry Ruklic

Helicopter Program

Clearwater / Nez Perce

Helicopter Crewmember

GS-0462

Trainee Slot

Helicopter Crewmember

GS-0462-04 STEP

Jacob Quigley

Locsha RD FMO

Chris Gauthier