Processing of the JEFF-3.1 Cross Section Library into a Continuous Energy Monte Carlo Radiation Transport and Criticality Data Library

NEA-2006

May 2006

Index

1.	Introduction: Report contents	7

2.	Processing evaluated nuclear data to ACE format.	9

2.1.	NJOY inputs to process Cross Section in ACE format	11

2.1.1.	NJOY step by step	12

2.1.2.	JEFF-3.1 ACE library.	16

2.2.	NJOY inputs to process ACE Thermal Scattering Libraries	25

2.3.	QA procedure	29

2.3.1.	Checking NJOY ouput messages for each material.	29

2.3.2.	Checking ACE libraries	34

2.3.3.	Q&A with ACELST code	42

2.3.4.	Example of Q&A with ACELST code: Fe56	43

2.4.	Differences: PREPRO-2004 versus NJOY99	49

2.4.1.	Case Tl0.nat	49

2.4.2.	Total cross sections	51

2.4.3.	Resonances	53

2.4.4.	Case: Co58	61

3.	NJOY99.90 + updates to process ACE library.	63

3.1.	NJOY99.90	63

3.2.	NJOY99.90+NEA updates	63

3.3.	NJOY99.112+JEFF3.1-updates	65

4.	Conversion of the library: makxsf	67

5.	Validation	69

5.1.	Criticality Validation	69

5.1.1.	LANL Validation Suite	70

5.1.2.	Additional Validation	76

5.2.	Radiation-Shielding validation Suite	77

5.2.1.	EURAC-Fe	77

5.2.2.	KANT	78

5.2.3.	VENUS	79

5.2.4.	NIST	80

5.2.4.1.	NoCd+NoWater+2,0"	80

5.2.4.2.	Cd+Water+2,5"	80

5.2.5.	IPPE-FE	81

5.2.6.	FNS: Oxygen	82

5.2.7.	Oktavian: Al	83

5.2.8.	LLNL Pulsed Spheres: Iron, 4.8 MFP	84

6.	References	85

APENDIX A	87

A.1 Be at 1200K	87

A.2 Be in BeO at 1200K	88

A.3 D in D2O at 643.9K	89

A.4 H in H2O at 1000K	90

A.5 H in HZr at 1200K	91

A.6 H in CH2 at 350K	92

A.7 Graphite  at 3000K	93

APENDIX B	95

B.1 Ag109 at 1200K (without PURR module)	95

B.2 U235 at 300K (with PURR module)	96

APENDIX C	97

C.1 upn90_noup63_noup56	97

C.2 uplf95	163

C.3 upn_Trkov	164

C.4 upn_Mattes	168

C.5 upn_Aldama	171

C.6 upn_Hogenbirk	172

C.7 upn_Sublet	194

C.8 upn_ADS	195

C.9 upn_CAD	197

C.10 upn_Shimizu	208

C.11 upn_Cabellos	218

C.12 upn_Leichtle_Mod	219

C.13 upn_Pescarini	227

APENDIX D. LANL Validation Suite	229

D.1 Jezebel: PU-MET-FAST-001	229

D.2 Jezebel-240: PU-MET-FAST-002	230

D3. Pu Buttons: PU-MET-FAST-003, case 103	231

D4. Flattop-Pu : PU-MET-FAST-006	233

D5. THOR: PU-MET-FAST-008	234

D6. PU-MET-FAST-011	235

D7. HISS/HPG : 	PU-COMP-INTER-001	236

D8. PNL-2: PU-SOL-THERM-021, case 3	237

D9. Jezebel-233:U233-MET-FAST-001	238

D10. Flattop-23: U233-MET-FAST-006	239

D11. U233-MF-05: U233-MET-FAST-005, case 2	240

D12. Falstaff-1: U233-SOL-INTER-001, case 1	241

D13. SB-2½:U233-COMP-THERM-001, case 3	242

D14. ORNL-11: U233-SOL-THERM-008	245

D15. Godiva: HEU-MET-FAST-001	246

D16. Flattop-25: HEU-MET-FAST-028	247

D17. Godiver: HEU-MET-FAST-004	248

D18. Zeus-2: HEU-MET-INTER-006, case 2	249

D19. SB-5: U233-COMP-THERM-001, case 6	252

D20. ORNL-10: HEU-SOL-THERM-032	256

D21. IEU-MF-03: IEU-MET-FAST-003	257

D22. BIG TEN: IEU-MET-FAST-007	261

D23. IEU-MF-04: IEU-MET-FAST-004	266

D24. Zebra-8H: MIX-MET-FAST-008, case 7	268

D25. IEU-CT-02: IEU-COMP-THERM-002, case 3	270

D26. STACY-36: LEU-SOL-THERM-007, case 36	275

D27. B&W XI-2: LEU-COMP-THERM-008, case 2	277

D28. LEU-ST-02: LEU-SOL-THERM-002, case 2	330

APENDIX E. Additional Criticality Validation	331

E.1 PU-SOL-THERM-009	331

E.2 HEU-MET-FAST-73	332

E.3 HEU-SOL-THERM-004_case1	335

E.4 SPEC-MET-FAST-08	336

APENDIX F. Radiation-Shielding validation Suite	339

F1. EURAC-Fe	339

F2. KANT	344

F3. NIST	349

F3.1 NoCd+NoWater+2,0"	349

F3.2 Cd+Water+2,5"	355

F4. IPPE-FE	362

F5. FNS_Oxygen	364

F6. Oktavian Al	368

F7. LLNL Pulsed Spheres: Iron, 4.8 MFP	370

# Introduction: Report contents

The source of the evaluated nuclear data is JEFF-3.1 [JEFF-3.1] being one the most recent released evaluated nuclear data library. The library comprises 381 materials and some thermal scattering evaluations.

The processing code system to be used is NJOY99  [NJOY-99] and in particular the ACER module.

A multi-temperature ACE-format neutron library for a wide range of up to ten temperatures depending on the application needs: 300, 400, 500, 600, 700, 800, 900, 1000,1200 and 1800 degrees Kelvin.

The processed data also contains production and gas production data whenever such data are contained in JEFF-3.1. Kinematic KERMA factors and total damage energy production data are processed.

The nuclides to be processed are all those of the General Purpose Library and Thermal Scattering Library, including important light nuclei, the structural materials, the fission products, control rod materials and burnable poisons, all major an minor actinides.

Some patches to the processing code NJOY are needed, and they are provided together with the library as well as the documentation. The inputs used for the processing are also included.

The library at 300K has been verified: visually (no discontinuities, correct processing in all range) and with comparisons with other libraries available for the same purposes (ENDF/B-VI.8, JEF2.2, JENDL3.3, …)

A set of experiments using MCNP4c [MCNP4c] are used in order to validate the processed library.

# Processing evaluated nuclear data to ACE format.

NJOY is a modular computer code used for converting evaluated nuclear data in the ENDF format into different type of libraries useful for applications calculations.

The JEFF-3.1 evaluated nuclear data file has been processed using NJOY-99.90 modular code system with some additional updates. The patch up90 was not able to process the whole JEFF-3.1 library.

The processing sequence for generating ACE-formatted library suitable for use by the MCNP4c code is shown below.

Figure 2.1. NJOY processing sequence for an ACE-format neutron library

The list of NJOY modules can be described by:

- MODER: Convert between ENDF/B standard coded mode and the NJOY blocked binary mode

- RECONR: Reconstruct pointwise cross sections from ENDF resonance parameters and interpolation schemes

- BROADR: Doppler-broadens and thins pointwise cross sections

- HEATR: Generate pointwise heat production cross section (KERMA factors) and radiation damage production cross sections

- GASPR: Add gas production to PENDF

- THERMR: Generate neutron scattering cross sections and point-to-point scattering kernels in the thermal range for free or bound atoms

- PURR: Prepare unresolved region probability tables for the MCNP continuous energy Monte Carlo code

- ACER: Prepare libraries in ACE format for the Los Alamos continuous energy Monte Carlo code MCNP

For each material the processing sequence can be divided into two calculations:

- First calculation, to produce point-wise data in ENDF format

- Second calculation, the module ACER generates the ACE formatted file that can be directly used in MCNP calculations. Here, error checking and consistency checks are also performed.

## NJOY inputs to process Cross Section in ACE format

The NJOY processing system is a modular computer code used for processing JEFF-3.1 into ACE format. Each module performs a well-defined processing task. These modules are linked by input and output files (tapes).

We have prepared a reference input file for each material and at a specific temperature. An example of NJOY input is given in Figure 2.2. The complete set of inputs is available through NEA Data Bank.

Figure 2.2. NJOY input used to generate ACE library for Ac225 (code 8925) at 300K.

### NJOY step by step

The ACE files have been processed following the specifications given in Refs. [ANRCP-1999-28, ADS-Lib/V1.0, ALEPH-DLG, ENDF2ACE, LA-UR-02-1235, LA-UR-03-0954, NJOY-99, YUCCA]. We present a summary of the most important processing options used by NJOY in a typical input file (Ac-225 at 300K).

MODER

Convert ENDF “tapes” back and forth between formatted (that is, ASCII, EBCDIC, etc.) and blocked binary modes.

- Input unit: 		20 (tape20, JEFF-3.1 cross section library)

- Material:		8925 (Ac-225)

MODER reads the JEFF-3.1 file (tape20) which contains the material (for Ac-225 the material number is 8925), extract it and put the ENDF file in binary mode in tape21.

RECONR

Reconstruct pointwise (energy-dependent) cross sections from ENDF resonance parameters and interpolation schemes.

- Reconstruction tolerance: 		0.1%

- Resonance-integral-check tolerance:	0.3%

- Reconstruction temperature:		0.0 K

RECONR read tape21, extract material 8925 and reconstruct cross section at 0K with a reconstruction tolerance of 0.1%. The resulting pointwise cross section is written in tape22.

BROADR

Doppler-broadens and thins pointwise cross sections.

- Thinning tolerance: 		0.1%

- Integral criterion tolerance:	0.3%

- Maximum energy: Doppler broadening was force up to the upper energy limit of the resolve resonance range, but never above 2 MeV

- Temperature: 			300 K

BROADR reads tape21-tape22 and Doppler-broadens at 300K for material 8925.The tolerance used is 0.1%. The results are written in tape23.

HEATR

Generate pointwise heat production cross sections (KERMA factors) and radiation-damage-production cross sections.

- MT=302: 	Elastic

- MT=303:	Non-elastic

- MT=304: 	Inelastic

- MT=318: 	Fission

- MT=402: 	Capture

- MT=443: 	Total kinematic kerma

- MT=444: 	Total damage energy production

HEATR computes energy-balance heating and damage energy for material 8925 at 300K. Input files are tape21-tape23. The output file is tape24.

GASPR

Add gas production (mt203-207) to PENDF.

GASPR add gas production reactions to PENDF tape24. Output file is tape25

THERMR

Produce cross sections and energy-to-energy matrices for free or bound scatterers in the thermal energy range.

- Number of angles bins: 	12

- Tolerance:			0.1%

- Max. energy:			4 eV

- Scattering option: 		 221 (free gas)

- Temperature:			300 K

THERMR generates neutron scattering cross sections and point-to-point scattering kernels in the thermal range. The input file is only tape25, the output file is tape41. The generation of neutron scattering cross sections is doing for material 8925 with 12 equi-probable angles at 300K. Free gas option is chosen and no elastic cross sections in the thermal range. A tolerance of 0.1% and the maximum energy for thermal treatment is 4 eV.

PURR

Prepare unresolved-region probability tables for the MCNP continuous-energy Monte Carlo code.

- Number of probability bins: 		  20

- Number of resonance ladders: 	100

- Temperature: 				300 K

- Bondarenko 0 value:   		1.0E+10

PURR calculates probability tables for treating unresolved-resonance self-shielding for Monte Carlo codes. Inputs tgape21-tape41, output in tape 26. Calculation performed for material 8925 at 300K with one 0 value (1.0E+10, infinite dilute cross section). A total number of 20 probability bins and 100 resonance ladders were selected.

ACER (cross section libraries)

Prepare libraries in ACE format for the Los Alamos continuous-energy Monte Carlo code MCNP.

- Type of ACE file: 		1 (ascii)

- ZAID suffix: 			.31

- No thinning

- Temperature: 			300 K

ACER prepares a data library for MCNP (in ASCII). Input files: tape21-26, output files: tape27 (ACE file) and tape28 (XSDIR file). The material processed is 8925 at 300K. The id suffix for this material is .31.

Second ACER module checks previous ACE file and prepare new tape29(ACE file) and tape30(XSDIR file).

### JEFF-3.1 ACE library.

The library contains pointwise cross section data files for use in the Monte Carlo code MCNP.

For each material two files were given:

- Cross section data file in the ACE type 1 (ASCII) format: 	file.ace

- Information required by xsdir file of MCNP code system: 	file.dir

These files were rewritten by the UpdXSDIR code [UpdXSDIR] to give the correct ACE filename and to update the route to 0.

Both files were prepared by the ACER module of NJOY-99. Also, probability tables (ptable) have been generated for those materials with unresolved resonance data.

Table 2.1. Information on the JEFF-3.1 ACE library at 300K.

| No. | Nuclide | ZAID | PT Tables | ACE filename | XSDIR filename |
| --- | --- | --- | --- | --- | --- |
| 1 | 1-H - 1 | 1001.31c | - | H1.ACE | H1.DIR |
| 2 | 1-H - 2 | 1002.31c | - | H2.ACE | H2.DIR |
| 3 | 1-H - 3 | 1003.31c | - | H3.ACE | H3.DIR |
| 4 | 2-He- 3 | 2003.31c | - | He3.ACE | He3.DIR |
| 5 | 2-He- 4 | 2004.31c | - | He4.ACE | He4.DIR |
| 6 | 3-Li- 6 | 3006.31c | - | Li6.ACE | Li6.DIR |
| 7 | 3-Li- 7 | 3007.31c | - | Li7.ACE | Li7.DIR |
| 8 | 4-Be- 9 | 4009.31c | - | Be9.ACE | Be9.DIR |
| 9 | 5-B - 10 | 5010.31c | - | B10.ACE | B10.DIR |
| 10 | 5-B - 11 | 5011.31c | - | B11.ACE | B11.DIR |
| 11 | 6-C - 0 | 6000.31c | - | C0.ACE | C0.DIR |
| 12 | 7-N - 14 | 7014.31c | - | N14.ACE | N14.DIR |
| 13 | 7-N - 15 | 7015.31c | - | N15.ACE | N15.DIR |
| 14 | 8-O - 16 | 8016.31c | - | O16.ACE | O16.DIR |
| 15 | 8-O - 17 | 8017.31c | - | O17.ACE | O17.DIR |
| 16 | 9-F - 19 | 9019.31c | - | F19.ACE | F19.DIR |
| 17 | 11-Na- 22 | 11022.31c | ptable | Na22.ACE | Na22.DIR |
| 18 | 11-Na- 23 | 11023.31c | - | Na23.ACE | Na23.DIR |
| 19 | 12-Mg- 24 | 12024.31c | - | Mg24.ACE | Mg24.DIR |
| 20 | 12-Mg- 25 | 12025.31c | - | Mg25.ACE | Mg25.DIR |
| 21 | 12-Mg- 26 | 12026.31c | - | Mg26.ACE | Mg26.DIR |
| 22 | 13-Al- 27 | 13027.31c | - | Al27.ACE | Al27.DIR |
| 23 | 14-Si- 28 | 14028.31c | - | Si28.ACE | Si28.DIR |
| 24 | 14-Si- 29 | 14029.31c | - | Si29.ACE | Si29.DIR |
| 25 | 14-Si- 30 | 14030.31c | - | Si30.ACE | Si30.DIR |
| 26 | 15-P - 31 | 15031.31c | - | P31.ACE | P31.DIR |
| 27 | 16-S - 32 | 16032.31c | - | S32.ACE | S32.DIR |
| 28 | 16-S - 33 | 16033.31c | - | S33.ACE | S33.DIR |
| 29 | 16-S - 34 | 16034.31c | - | S34.ACE | S34.DIR |
| 30 | 16-S - 36 | 16036.31c | - | S36.ACE | S36.DIR |
| 31 | 17-Cl- 35 | 17035.31c | - | Cl35.ACE | Cl35.DIR |
| 32 | 17-Cl- 37 | 17037.31c | - | Cl37.ACE | Cl37.DIR |
| 33 | 18-Ar- 36 | 18036.31c | ptable | Ar36.ACE | Ar36.DIR |
| 34 | 18-Ar- 38 | 18038.31c | ptable | Ar38.ACE | Ar38.DIR |
| 35 | 18-Ar- 40 | 18040.31c | - | Ar40.ACE | Ar40.DIR |
| 36 | 19-K - 39 | 19039.31c | - | K39.ACE | K39.DIR |
| 37 | 19-K - 40 | 19040.31c | - | K40.ACE | K40.DIR |
| 38 | 19-K - 41 | 19041.31c | - | K41.ACE | K41.DIR |
| 39 | 20-Ca- 40 | 20040.31c | - | Ca40.ACE | Ca40.DIR |
| 40 | 20-Ca- 42 | 20042.31c | - | Ca42.ACE | Ca42.DIR |
| 41 | 20-Ca- 43 | 20043.31c | - | Ca43.ACE | Ca43.DIR |
| 42 | 20-Ca- 44 | 20044.31c | - | Ca44.ACE | Ca44.DIR |
| 43 | 20-Ca- 46 | 20046.31c | - | Ca46.ACE | Ca46.DIR |
| 44 | 20-Ca- 48 | 20048.31c | - | Ca48.ACE | Ca48.DIR |
| 45 | 21-Sc- 45 | 21045.31c | - | Sc45.ACE | Sc45.DIR |
| 46 | 22-Ti- 46 | 22046.31c | - | Ti46.ACE | Ti46.DIR |
| 47 | 22-Ti- 47 | 22047.31c | - | Ti47.ACE | Ti47.DIR |
| 48 | 22-Ti- 48 | 22048.31c | - | Ti48.ACE | Ti48.DIR |
| 49 | 22-Ti- 49 | 22049.31c | - | Ti49.ACE | Ti49.DIR |
| 50 | 22-Ti- 50 | 22050.31c | - | Ti50.ACE | Ti50.DIR |
| 51 | 23-V - 0 | 23000.31c | - | V0.ACE | V0.DIR |
| 52 | 24-Cr- 50 | 24050.31c | - | Cr50.ACE | Cr50.DIR |
| 53 | 24-Cr- 52 | 24052.31c | - | Cr52.ACE | Cr52.DIR |
| 54 | 24-Cr- 53 | 24053.31c | - | Cr53.ACE | Cr53.DIR |
| 55 | 24-Cr- 54 | 24054.31c | - | Cr54.ACE | Cr54.DIR |
| 56 | 25-Mn- 55 | 25055.31c | - | Mn55.ACE | Mn55.DIR |
| 57 | 26-Fe- 54 | 26054.31c | - | Fe54.ACE | Fe54.DIR |
| 58 | 26-Fe- 56 | 26056.31c | - | Fe56.ACE | Fe56.DIR |
| 59 | 26-Fe- 57 | 26057.31c | - | Fe57.ACE | Fe57.DIR |
| 60 | 26-Fe- 58 | 26058.31c | ptable | Fe58.ACE | Fe58.DIR |
| 61 | 27-Co- 58 | 27108.31c | - | Co58M.ACE | Co58M.DIR |
| 62 | 27-Co- 58 | 27058.31c | - | Co58.ACE | Co58.DIR |
| 63 | 27-Co- 59 | 27059.31c | - | Co59.ACE | Co59.DIR |
| 64 | 28-Ni- 58 | 28058.31c | - | Ni58.ACE | Ni58.DIR |
| 65 | 28-Ni- 59 | 28059.31c | - | Ni59.ACE | Ni59.DIR |
| 66 | 28-Ni- 60 | 28060.31c | - | Ni60.ACE | Ni60.DIR |
| 67 | 28-Ni- 61 | 28061.31c | - | Ni61.ACE | Ni61.DIR |
| 68 | 28-Ni- 62 | 28062.31c | - | Ni62.ACE | Ni62.DIR |
| 69 | 28-Ni- 64 | 28064.31c | - | Ni64.ACE | Ni64.DIR |
| 70 | 29-Cu- 63 | 29063.31c | - | Cu63.ACE | Cu63.DIR |
| 71 | 29-Cu- 65 | 29065.31c | - | Cu65.ACE | Cu65.DIR |
| 72 | 30-Zn- 0 | 30000.31c | - | Zn0.ACE | Zn0.DIR |
| 73 | 31-Ga- 0 | 31000.31c | - | Ga0.ACE | Ga0.DIR |
| 74 | 32-Ge- 70 | 32070.31c | - | Ge70.ACE | Ge70.DIR |
| 75 | 32-Ge- 72 | 32072.31c | - | Ge72.ACE | Ge72.DIR |
| 76 | 32-Ge- 73 | 32073.31c | - | Ge73.ACE | Ge73.DIR |
| 77 | 32-Ge- 74 | 32074.31c | - | Ge74.ACE | Ge74.DIR |
| 78 | 32-Ge- 76 | 32076.31c | - | Ge76.ACE | Ge76.DIR |
| 79 | 33-As- 75 | 33075.31c | - | As75.ACE | As75.DIR |
| 80 | 34-Se- 74 | 34074.31c | - | Se74.ACE | Se74.DIR |
| 81 | 34-Se- 76 | 34076.31c | - | Se76.ACE | Se76.DIR |
| 82 | 34-Se- 77 | 34077.31c | - | Se77.ACE | Se77.DIR |
| 83 | 34-Se- 78 | 34078.31c | - | Se78.ACE | Se78.DIR |
| 84 | 34-Se- 79 | 34079.31c | ptable | Se79.ACE | Se79.DIR |
| 85 | 34-Se- 80 | 34080.31c | - | Se80.ACE | Se80.DIR |
| 86 | 34-Se- 82 | 34082.31c | - | Se82.ACE | Se82.DIR |
| 87 | 35-Br- 79 | 35079.31c | - | Br79.ACE | Br79.DIR |
| 88 | 35-Br- 81 | 35081.31c | - | Br81.ACE | Br81.DIR |
| 89 | 36-Kr- 78 | 36078.31c | - | Kr78.ACE | Kr78.DIR |
| 90 | 36-Kr- 80 | 36080.31c | - | Kr80.ACE | Kr80.DIR |
| 91 | 36-Kr- 82 | 36082.31c | - | Kr82.ACE | Kr82.DIR |
| 92 | 36-Kr- 83 | 36083.31c | - | Kr83.ACE | Kr83.DIR |
| 93 | 36-Kr- 84 | 36084.31c | - | Kr84.ACE | Kr84.DIR |
| 94 | 36-Kr- 85 | 36085.31c | - | Kr85.ACE | Kr85.DIR |
| 95 | 36-Kr- 86 | 36086.31c | - | Kr86.ACE | Kr86.DIR |
| 96 | 37-Rb- 85 | 37085.31c | - | Rb85.ACE | Rb85.DIR |
| 97 | 37-Rb- 86 | 37086.31c | - | Rb86.ACE | Rb86.DIR |
| 98 | 37-Rb- 87 | 37087.31c | - | Rb87.ACE | Rb87.DIR |
| 99 | 38-Sr- 84 | 38084.31c | - | Sr84.ACE | Sr84.DIR |
| 100 | 38-Sr- 86 | 38086.31c | - | Sr86.ACE | Sr86.DIR |
| 101 | 38-Sr- 87 | 38087.31c | - | Sr87.ACE | Sr87.DIR |
| 102 | 38-Sr- 88 | 38088.31c | - | Sr88.ACE | Sr88.DIR |
| 103 | 38-Sr- 89 | 38089.31c | - | Sr89.ACE | Sr89.DIR |
| 104 | 38-Sr- 90 | 38090.31c | - | Sr90.ACE | Sr90.DIR |
| 105 | 39-Y - 89 | 39089.31c | - | Y89.ACE | Y89.DIR |
| 106 | 39-Y - 90 | 39090.31c | - | Y90.ACE | Y90.DIR |
| 107 | 39-Y - 91 | 39091.31c | - | Y91.ACE | Y91.DIR |
| 108 | 40-Zr- 90 | 40090.31c | - | Zr90.ACE | Zr90.DIR |
| 109 | 40-Zr- 91 | 40091.31c | ptable | Zr91.ACE | Zr91.DIR |
| 110 | 40-Zr- 92 | 40092.31c | ptable | Zr92.ACE | Zr92.DIR |
| 111 | 40-Zr- 93 | 40093.31c | ptable | Zr93.ACE | Zr93.DIR |
| 112 | 40-Zr- 94 | 40094.31c | ptable | Zr94.ACE | Zr94.DIR |
| 113 | 40-Zr- 95 | 40095.31c | ptable | Zr95.ACE | Zr95.DIR |
| 114 | 40-Zr- 96 | 40096.31c | - | Zr96.ACE | Zr96.DIR |
| 115 | 41-Nb- 93 | 41093.31c | - | Nb93.ACE | Nb93.DIR |
| 116 | 41-Nb- 94 | 41094.31c | ptable | Nb94.ACE | Nb94.DIR |
| 117 | 41-Nb- 95 | 41095.31c | ptable | Nb95.ACE | Nb95.DIR |
| 118 | 42-Mo- 92 | 42092.31c | ptable | Mo92.ACE | Mo92.DIR |
| 119 | 42-Mo- 94 | 42094.31c | ptable | Mo94.ACE | Mo94.DIR |
| 120 | 42-Mo- 95 | 42095.31c | ptable | Mo95.ACE | Mo95.DIR |
| 121 | 42-Mo- 96 | 42096.31c | ptable | Mo96.ACE | Mo96.DIR |
| 122 | 42-Mo- 97 | 42097.31c | ptable | Mo97.ACE | Mo97.DIR |
| 123 | 42-Mo- 98 | 42098.31c | ptable | Mo98.ACE | Mo98.DIR |
| 124 | 42-Mo- 99 | 42099.31c | ptable | Mo99.ACE | Mo99.DIR |
| 125 | 42-Mo-100 | 42100.31c | ptable | Mo100.ACE | Mo100.DIR |
| 126 | 43-Tc- 99 | 43099.31c | ptable | Tc99.ACE | Tc99.DIR |
| 127 | 44-Ru- 96 | 44096.31c | - | Ru96.ACE | Ru96.DIR |
| 128 | 44-Ru- 98 | 44098.31c | - | Ru98.ACE | Ru98.DIR |
| 129 | 44-Ru- 99 | 44099.31c | - | Ru99.ACE | Ru99.DIR |
| 130 | 44-Ru-100 | 44100.31c | - | Ru100.ACE | Ru100.DIR |
| 131 | 44-Ru-101 | 44101.31c | ptable | Ru101.ACE | Ru101.DIR |
| 132 | 44-Ru-102 | 44102.31c | - | Ru102.ACE | Ru102.DIR |
| 133 | 44-Ru-103 | 44103.31c | ptable | Ru103.ACE | Ru103.DIR |
| 134 | 44-Ru-104 | 44104.31c | - | Ru104.ACE | Ru104.DIR |
| 135 | 44-Ru-105 | 44105.31c | - | Ru105.ACE | Ru105.DIR |
| 136 | 44-Ru-106 | 44106.31c | - | Ru106.ACE | Ru106.DIR |
| 137 | 45-Rh-103 | 45103.31c | - | Rh103.ACE | Rh103.DIR |
| 138 | 45-Rh-105 | 45105.31c | - | Rh105.ACE | Rh105.DIR |
| 139 | 46-Pd-102 | 46102.31c | - | Pd102.ACE | Pd102.DIR |
| 140 | 46-Pd-104 | 46104.31c | ptable | Pd104.ACE | Pd104.DIR |
| 141 | 46-Pd-105 | 46105.31c | ptable | Pd105.ACE | Pd105.DIR |
| 142 | 46-Pd-106 | 46106.31c | ptable | Pd106.ACE | Pd106.DIR |
| 143 | 46-Pd-107 | 46107.31c | ptable | Pd107.ACE | Pd107.DIR |
| 144 | 46-Pd-108 | 46108.31c | ptable | Pd108.ACE | Pd108.DIR |
| 145 | 46-Pd-110 | 46110.31c | ptable | Pd110.ACE | Pd110.DIR |
| 146 | 47-Ag-107 | 47107.31c | - | Ag107.ACE | Ag107.DIR |
| 147 | 47-Ag-109 | 47109.31c | ptable | Ag109.ACE | Ag109.DIR |
| 148 | 47-Ag-110 | 47160.31c | ptable | Ag110M.ACE | Ag110M.DIR |
| 149 | 47-Ag-111 | 47111.31c | - | Ag111.ACE | Ag111.DIR |
| 150 | 48-Cd-106 | 48106.31c | ptable | Cd106.ACE | Cd106.DIR |
| 151 | 48-Cd-108 | 48108.31c | ptable | Cd108.ACE | Cd108.DIR |
| 152 | 48-Cd-110 | 48110.31c | ptable | Cd110.ACE | Cd110.DIR |
| 153 | 48-Cd-111 | 48111.31c | - | Cd111.ACE | Cd111.DIR |
| 154 | 48-Cd-112 | 48112.31c | ptable | Cd112.ACE | Cd112.DIR |
| 155 | 48-Cd-113 | 48113.31c | - | Cd113.ACE | Cd113.DIR |
| 156 | 48-Cd-114 | 48114.31c | ptable | Cd114.ACE | Cd114.DIR |
| 157 | 48-Cd-115 | 48165.31c | - | Cd115M.ACE | Cd115M.DIR |
| 158 | 48-Cd-116 | 48116.31c | ptable | Cd116.ACE | Cd116.DIR |
| 159 | 49-In-113 | 49113.31c | ptable | In113.ACE | In113.DIR |
| 160 | 49-In-115 | 49115.31c | ptable | In115.ACE | In115.DIR |
| 161 | 50-Sn-112 | 50112.31c | ptable | Sn112.ACE | Sn112.DIR |
| 162 | 50-Sn-114 | 50114.31c | ptable | Sn114.ACE | Sn114.DIR |
| 163 | 50-Sn-115 | 50115.31c | ptable | Sn115.ACE | Sn115.DIR |
| 164 | 50-Sn-116 | 50116.31c | ptable | Sn116.ACE | Sn116.DIR |
| 165 | 50-Sn-117 | 50117.31c | ptable | Sn117.ACE | Sn117.DIR |
| 166 | 50-Sn-118 | 50118.31c | ptable | Sn118.ACE | Sn118.DIR |
| 167 | 50-Sn-119 | 50119.31c | ptable | Sn119.ACE | Sn119.DIR |
| 168 | 50-Sn-120 | 50120.31c | ptable | Sn120.ACE | Sn120.DIR |
| 169 | 50-Sn-122 | 50122.31c | ptable | Sn122.ACE | Sn122.DIR |
| 170 | 50-Sn-123 | 50123.31c | - | Sn123.ACE | Sn123.DIR |
| 171 | 50-Sn-124 | 50124.31c | ptable | Sn124.ACE | Sn124.DIR |
| 172 | 50-Sn-125 | 50125.31c | - | Sn125.ACE | Sn125.DIR |
| 173 | 50-Sn-126 | 50126.31c | - | Sn126.ACE | Sn126.DIR |
| 174 | 51-Sb-121 | 51121.31c | ptable | Sb121.ACE | Sb121.DIR |
| 175 | 51-Sb-123 | 51123.31c | ptable | Sb123.ACE | Sb123.DIR |
| 176 | 51-Sb-124 | 51124.31c | - | Sb124.ACE | Sb124.DIR |
| 177 | 51-Sb-125 | 51125.31c | - | Sb125.ACE | Sb125.DIR |
| 178 | 51-Sb-126 | 51126.31c | - | Sb126.ACE | Sb126.DIR |
| 179 | 52-Te-120 | 52120.31c | - | Te120.ACE | Te120.DIR |
| 180 | 52-Te-122 | 52122.31c | - | Te122.ACE | Te122.DIR |
| 181 | 52-Te-123 | 52123.31c | - | Te123.ACE | Te123.DIR |
| 182 | 52-Te-124 | 52124.31c | - | Te124.ACE | Te124.DIR |
| 183 | 52-Te-125 | 52125.31c | - | Te125.ACE | Te125.DIR |
| 184 | 52-Te-126 | 52126.31c | - | Te126.ACE | Te126.DIR |
| 185 | 52-Te-127 | 52177.31c | - | Te127M.ACE | Te127M.DIR |
| 186 | 52-Te-128 | 52128.31c | - | Te128.ACE | Te128.DIR |
| 187 | 52-Te-129 | 52179.31c | - | Te129M.ACE | Te129M.DIR |
| 188 | 52-Te-130 | 52130.31c | - | Te130.ACE | Te130.DIR |
| 189 | 52-Te-132 | 52132.31c | - | Te132.ACE | Te132.DIR |
| 190 | 53-I -127 | 53127.31c | - | I127.ACE | I127.DIR |
| 191 | 53-I -129 | 53129.31c | - | I129.ACE | I129.DIR |
| 192 | 53-I -130 | 53130.31c | - | I130.ACE | I130.DIR |
| 193 | 53-I -131 | 53131.31c | - | I131.ACE | I131.DIR |
| 194 | 53-I -135 | 53135.31c | - | I135.ACE | I135.DIR |
| 195 | 54-Xe-124 | 54124.31c | - | Xe124.ACE | Xe124.DIR |
| 196 | 54-Xe-126 | 54126.31c | - | Xe126.ACE | Xe126.DIR |
| 197 | 54-Xe-128 | 54128.31c | - | Xe128.ACE | Xe128.DIR |
| 198 | 54-Xe-129 | 54129.31c | - | Xe129.ACE | Xe129.DIR |
| 199 | 54-Xe-130 | 54130.31c | - | Xe130.ACE | Xe130.DIR |
| 200 | 54-Xe-131 | 54131.31c | - | Xe131.ACE | Xe131.DIR |
| 201 | 54-Xe-132 | 54132.31c | - | Xe132.ACE | Xe132.DIR |
| 202 | 54-Xe-133 | 54133.31c | - | Xe133.ACE | Xe133.DIR |
| 203 | 54-Xe-134 | 54134.31c | - | Xe134.ACE | Xe134.DIR |
| 204 | 54-Xe-135 | 54135.31c | - | Xe135.ACE | Xe135.DIR |
| 205 | 54-Xe-136 | 54136.31c | - | Xe136.ACE | Xe136.DIR |
| 206 | 55-Cs-133 | 55133.31c | ptable | Cs133.ACE | Cs133.DIR |
| 207 | 55-Cs-134 | 55134.31c | - | Cs134.ACE | Cs134.DIR |
| 208 | 55-Cs-135 | 55135.31c | ptable | Cs135.ACE | Cs135.DIR |
| 209 | 55-Cs-136 | 55136.31c | - | Cs136.ACE | Cs136.DIR |
| 210 | 55-Cs-137 | 55137.31c | ptable | Cs137.ACE | Cs137.DIR |
| 211 | 56-Ba-130 | 56130.31c | ptable | Ba130.ACE | Ba130.DIR |
| 212 | 56-Ba-132 | 56132.31c | ptable | Ba132.ACE | Ba132.DIR |
| 213 | 56-Ba-134 | 56134.31c | ptable | Ba134.ACE | Ba134.DIR |
| 214 | 56-Ba-135 | 56135.31c | ptable | Ba135.ACE | Ba135.DIR |
| 215 | 56-Ba-136 | 56136.31c | ptable | Ba136.ACE | Ba136.DIR |
| 216 | 56-Ba-137 | 56137.31c | ptable | Ba137.ACE | Ba137.DIR |
| 217 | 56-Ba-138 | 56138.31c | - | Ba138.ACE | Ba138.DIR |
| 218 | 56-Ba-140 | 56140.31c | ptable | Ba140.ACE | Ba140.DIR |
| 219 | 57-La-138 | 57138.31c | ptable | La138.ACE | La138.DIR |
| 220 | 57-La-139 | 57139.31c | ptable | La139.ACE | La139.DIR |
| 221 | 57-La-140 | 57140.31c | - | La140.ACE | La140.DIR |
| 222 | 58-Ce-140 | 58140.31c | - | Ce140.ACE | Ce140.DIR |
| 223 | 58-Ce-141 | 58141.31c | ptable | Ce141.ACE | Ce141.DIR |
| 224 | 58-Ce-142 | 58142.31c | ptable | Ce142.ACE | Ce142.DIR |
| 225 | 58-Ce-143 | 58143.31c | - | Ce143.ACE | Ce143.DIR |
| 226 | 58-Ce-144 | 58144.31c | ptable | Ce144.ACE | Ce144.DIR |
| 227 | 59-Pr-141 | 59141.31c | ptable | Pr141.ACE | Pr141.DIR |
| 228 | 59-Pr-142 | 59142.31c | - | Pr142.ACE | Pr142.DIR |
| 229 | 59-Pr-143 | 59143.31c | - | Pr143.ACE | Pr143.DIR |
| 230 | 60-Nd-142 | 60142.31c | - | Nd142.ACE | Nd142.DIR |
| 231 | 60-Nd-143 | 60143.31c | ptable | Nd143.ACE | Nd143.DIR |
| 232 | 60-Nd-144 | 60144.31c | ptable | Nd144.ACE | Nd144.DIR |
| 233 | 60-Nd-145 | 60145.31c | ptable | Nd145.ACE | Nd145.DIR |
| 234 | 60-Nd-146 | 60146.31c | ptable | Nd146.ACE | Nd146.DIR |
| 235 | 60-Nd-147 | 60147.31c | - | Nd147.ACE | Nd147.DIR |
| 236 | 60-Nd-148 | 60148.31c | ptable | Nd148.ACE | Nd148.DIR |
| 237 | 60-Nd-150 | 60150.31c | - | Nd150.ACE | Nd150.DIR |
| 238 | 61-Pm-147 | 61147.31c | ptable | Pm147.ACE | Pm147.DIR |
| 239 | 61-Pm-148 | 61198.31c | - | Pm148M.ACE | Pm148M.DIR |
| 240 | 61-Pm-148 | 61148.31c | - | Pm148.ACE | Pm148.DIR |
| 241 | 61-Pm-149 | 61149.31c | - | Pm149.ACE | Pm149.DIR |
| 242 | 61-Pm-151 | 61151.31c | - | Pm151.ACE | Pm151.DIR |
| 243 | 62-Sm-144 | 62144.31c | - | Sm144.ACE | Sm144.DIR |
| 244 | 62-Sm-147 | 62147.31c | ptable | Sm147.ACE | Sm147.DIR |
| 245 | 62-Sm-148 | 62148.31c | - | Sm148.ACE | Sm148.DIR |
| 246 | 62-Sm-149 | 62149.31c | ptable | Sm149.ACE | Sm149.DIR |
| 247 | 62-Sm-150 | 62150.31c | - | Sm150.ACE | Sm150.DIR |
| 248 | 62-Sm-151 | 62151.31c | ptable | Sm151.ACE | Sm151.DIR |
| 249 | 62-Sm-152 | 62152.31c | ptable | Sm152.ACE | Sm152.DIR |
| 250 | 62-Sm-153 | 62153.31c | - | Sm153.ACE | Sm153.DIR |
| 251 | 62-Sm-154 | 62154.31c | - | Sm154.ACE | Sm154.DIR |
| 252 | 63-Eu-151 | 63151.31c | ptable | Eu151.ACE | Eu151.DIR |
| 253 | 63-Eu-152 | 63152.31c | ptable | Eu152.ACE | Eu152.DIR |
| 254 | 63-Eu-153 | 63153.31c | ptable | Eu153.ACE | Eu153.DIR |
| 255 | 63-Eu-154 | 63154.31c | ptable | Eu154.ACE | Eu154.DIR |
| 256 | 63-Eu-155 | 63155.31c | ptable | Eu155.ACE | Eu155.DIR |
| 257 | 63-Eu-156 | 63156.31c | - | Eu156.ACE | Eu156.DIR |
| 258 | 63-Eu-157 | 63157.31c | - | Eu157.ACE | Eu157.DIR |
| 259 | 64-Gd-152 | 64152.31c | ptable | Gd152.ACE | Gd152.DIR |
| 260 | 64-Gd-154 | 64154.31c | - | Gd154.ACE | Gd154.DIR |
| 261 | 64-Gd-155 | 64155.31c | ptable | Gd155.ACE | Gd155.DIR |
| 262 | 64-Gd-156 | 64156.31c | ptable | Gd156.ACE | Gd156.DIR |
| 263 | 64-Gd-157 | 64157.31c | - | Gd157.ACE | Gd157.DIR |
| 264 | 64-Gd-158 | 64158.31c | - | Gd158.ACE | Gd158.DIR |
| 265 | 64-Gd-160 | 64160.31c | - | Gd160.ACE | Gd160.DIR |
| 266 | 65-Tb-159 | 65159.31c | ptable | Tb159.ACE | Tb159.DIR |
| 267 | 65-Tb-160 | 65160.31c | - | Tb160.ACE | Tb160.DIR |
| 268 | 66-Dy-160 | 66160.31c | - | Dy160.ACE | Dy160.DIR |
| 269 | 66-Dy-161 | 66161.31c | ptable | Dy161.ACE | Dy161.DIR |
| 270 | 66-Dy-162 | 66162.31c | ptable | Dy162.ACE | Dy162.DIR |
| 271 | 66-Dy-163 | 66163.31c | - | Dy163.ACE | Dy163.DIR |
| 272 | 66-Dy-164 | 66164.31c | ptable | Dy164.ACE | Dy164.DIR |
| 273 | 67-Ho-165 | 67165.31c | - | Ho165.ACE | Ho165.DIR |
| 274 | 68-Er-162 | 68162.31c | - | Er162.ACE | Er162.DIR |
| 275 | 68-Er-164 | 68164.31c | - | Er164.ACE | Er164.DIR |
| 276 | 68-Er-166 | 68166.31c | - | Er166.ACE | Er166.DIR |
| 277 | 68-Er-167 | 68167.31c | ptable | Er167.ACE | Er167.DIR |
| 278 | 68-Er-168 | 68168.31c | - | Er168.ACE | Er168.DIR |
| 279 | 68-Er-170 | 68170.31c | - | Er170.ACE | Er170.DIR |
| 280 | 71-Lu-175 | 71175.31c | ptable | Lu175.ACE | Lu175.DIR |
| 281 | 71-Lu-176 | 71176.31c | ptable | Lu176.ACE | Lu176.DIR |
| 282 | 72-Hf-174 | 72174.31c | ptable | Hf174.ACE | Hf174.DIR |
| 283 | 72-Hf-176 | 72176.31c | ptable | Hf176.ACE | Hf176.DIR |
| 284 | 72-Hf-177 | 72177.31c | ptable | Hf177.ACE | Hf177.DIR |
| 285 | 72-Hf-178 | 72178.31c | ptable | Hf178.ACE | Hf178.DIR |
| 286 | 72-Hf-179 | 72179.31c | ptable | Hf179.ACE | Hf179.DIR |
| 287 | 72-Hf-180 | 72180.31c | ptable | Hf180.ACE | Hf180.DIR |
| 288 | 73-Ta-181 | 73181.31c | ptable | Ta181.ACE | Ta181.DIR |
| 289 | 73-Ta-182 | 73182.31c | ptable | Ta182.ACE | Ta182.DIR |
| 290 | 74-W -182 | 74182.31c | - | W182.ACE | W182.DIR |
| 291 | 74-W -183 | 74183.31c | - | W183.ACE | W183.DIR |
| 292 | 74-W -184 | 74184.31c | - | W184.ACE | W184.DIR |
| 293 | 74-W -186 | 74186.31c | - | W186.ACE | W186.DIR |
| 294 | 75-Re-185 | 75185.31c | ptable | Re185.ACE | Re185.DIR |
| 295 | 75-Re-187 | 75187.31c | ptable | Re187.ACE | Re187.DIR |
| 296 | 76-Os- 0 | 76000.31c | - | Os0.ACE | Os0.DIR |
| 297 | 77-Ir-191 | 77191.31c | ptable | Ir191.ACE | Ir191.DIR |
| 298 | 77-Ir-193 | 77193.31c | ptable | Ir193.ACE | Ir193.DIR |
| 299 | 78-Pt- 0 | 78000.31c | - | Pt0.ACE | Pt0.DIR |
| 300 | 79-Au-197 | 79197.31c | - | Au197.ACE | Au197.DIR |
| 301 | 80-Hg-196 | 80196.31c | - | Hg196.ACE | Hg196.DIR |
| 302 | 80-Hg-198 | 80198.31c | - | Hg198.ACE | Hg198.DIR |
| 303 | 80-Hg-199 | 80199.31c | - | Hg199.ACE | Hg199.DIR |
| 304 | 80-Hg-200 | 80200.31c | - | Hg200.ACE | Hg200.DIR |
| 305 | 80-Hg-201 | 80201.31c | - | Hg201.ACE | Hg201.DIR |
| 306 | 80-Hg-202 | 80202.31c | - | Hg202.ACE | Hg202.DIR |
| 307 | 80-Hg-204 | 80204.31c | - | Hg204.ACE | Hg204.DIR |
| 308 | 81-Tl- 0 | 81000.31c | - | Tl0.ACE | Tl0.DIR |
| 309 | 82-Pb-204 | 82204.31c | - | Pb204.ACE | Pb204.DIR |
| 310 | 82-Pb-206 | 82206.31c | - | Pb206.ACE | Pb206.DIR |
| 311 | 82-Pb-207 | 82207.31c | - | Pb207.ACE | Pb207.DIR |
| 312 | 82-Pb-208 | 82208.31c | - | Pb208.ACE | Pb208.DIR |
| 313 | 83-Bi-209 | 83209.31c | - | Bi209.ACE | Bi209.DIR |
| 314 | 88-Ra-223 | 88223.31c | - | Ra223.ACE | Ra223.DIR |
| 315 | 88-Ra-224 | 88224.31c | - | Ra224.ACE | Ra224.DIR |
| 316 | 88-Ra-225 | 88225.31c | - | Ra225.ACE | Ra225.DIR |
| 317 | 88-Ra-226 | 88226.31c | - | Ra226.ACE | Ra226.DIR |
| 318 | 89-Ac-225 | 89225.31c | - | Ac225.ACE | Ac225.DIR |
| 319 | 89-Ac-226 | 89226.31c | - | Ac226.ACE | Ac226.DIR |
| 320 | 89-Ac-227 | 89227.31c | - | Ac227.ACE | Ac227.DIR |
| 321 | 90-Th-227 | 90227.31c | - | Th227.ACE | Th227.DIR |
| 322 | 90-Th-228 | 90228.31c | - | Th228.ACE | Th228.DIR |
| 323 | 90-Th-229 | 90229.31c | - | Th229.ACE | Th229.DIR |
| 324 | 90-Th-230 | 90230.31c | - | Th230.ACE | Th230.DIR |
| 325 | 90-Th-232 | 90232.31c | ptable | Th232.ACE | Th232.DIR |
| 326 | 90-Th-233 | 90233.31c | - | Th233.ACE | Th233.DIR |
| 327 | 90-Th-234 | 90234.31c | - | Th234.ACE | Th234.DIR |
| 328 | 91-Pa-231 | 91231.31c | ptable | Pa231.ACE | Pa231.DIR |
| 329 | 91-Pa-232 | 91232.31c | - | Pa232.ACE | Pa232.DIR |
| 330 | 91-Pa-233 | 91233.31c | ptable | Pa233.ACE | Pa233.DIR |
| 331 | 92-U -232 | 92232.31c | ptable | U232.ACE | U232.DIR |
| 332 | 92-U -233 | 92233.31c | ptable | U233.ACE | U233.DIR |
| 333 | 92-U -234 | 92234.31c | ptable | U234.ACE | U234.DIR |
| 334 | 92-U -235 | 92235.31c | ptable | U235.ACE | U235.DIR |
| 335 | 92-U -236 | 92236.31c | - | U236.ACE | U236.DIR |
| 336 | 92-U -237 | 92237.31c | ptable | U237.ACE | U237.DIR |
| 337 | 92-U -238 | 92238.31c | ptable | U238.ACE | U238.DIR |
| 338 | 93-Np-235 | 93235.31c | - | Np235.ACE | Np235.DIR |
| 339 | 93-Np-236 | 93236.31c | - | Np236.ACE | Np236.DIR |
| 340 | 93-Np-237 | 93237.31c | ptable | Np237.ACE | Np237.DIR |
| 341 | 93-Np-238 | 93238.31c | ptable | Np238.ACE | Np238.DIR |
| 342 | 93-Np-239 | 93239.31c | - | Np239.ACE | Np239.DIR |
| 343 | 94-Pu-236 | 94236.31c | ptable | Pu236.ACE | Pu236.DIR |
| 344 | 94-Pu-237 | 94237.31c | - | Pu237.ACE | Pu237.DIR |
| 345 | 94-Pu-238 | 94238.31c | ptable | Pu238.ACE | Pu238.DIR |
| 346 | 94-Pu-239 | 94239.31c | ptable | Pu239.ACE | Pu239.DIR |
| 347 | 94-Pu-240 | 94240.31c | ptable | Pu240.ACE | Pu240.DIR |
| 348 | 94-Pu-241 | 94241.31c | ptable | Pu241.ACE | Pu241.DIR |
| 349 | 94-Pu-242 | 94242.31c | ptable | Pu242.ACE | Pu242.DIR |
| 350 | 94-Pu-243 | 94243.31c | ptable | Pu243.ACE | Pu243.DIR |
| 351 | 94-Pu-244 | 94244.31c | ptable | Pu244.ACE | Pu244.DIR |
| 352 | 94-Pu-246 | 94246.31c | - | Pu246.ACE | Pu246.DIR |
| 353 | 95-Am-241 | 95241.31c | ptable | Am241.ACE | Am241.DIR |
| 354 | 95-Am-242 | 95242.31c | ptable | Am242G.ACE | Am242G.DIR |
| 355 | 95-Am-242 | 95292.31c | ptable | Am242M.ACE | Am242M.DIR |
| 356 | 95-Am-243 | 95243.31c | ptable | Am243.ACE | Am243.DIR |
| 357 | 95-Am-244 | 95294.31c | - | Am244M.ACE | Am244M.DIR |
| 358 | 95-Am-244 | 95244.31c | - | Am244.ACE | Am244.DIR |
| 359 | 96-Cm-240 | 96240.31c | ptable | Cm240.ACE | Cm240.DIR |
| 360 | 96-Cm-241 | 96241.31c | - | Cm241.ACE | Cm241.DIR |
| 361 | 96-Cm-242 | 96242.31c | ptable | Cm242.ACE | Cm242.DIR |
| 362 | 96-Cm-243 | 96243.31c | ptable | Cm243.ACE | Cm243.DIR |
| 363 | 96-Cm-244 | 96244.31c | ptable | Cm244.ACE | Cm244.DIR |
| 364 | 96-Cm-245 | 96245.31c | ptable | Cm245.ACE | Cm245.DIR |
| 365 | 96-Cm-246 | 96246.31c | ptable | Cm246.ACE | Cm246.DIR |
| 366 | 96-Cm-247 | 96247.31c | ptable | Cm247.ACE | Cm247.DIR |
| 367 | 96-Cm-248 | 96248.31c | ptable | Cm248.ACE | Cm248.DIR |
| 368 | 96-Cm-249 | 96249.31c | ptable | Cm249.ACE | Cm249.DIR |
| 369 | 96-Cm-250 | 96250.31c | ptable | Cm250.ACE | Cm250.DIR |
| 370 | 97-Bk-247 | 97247.31c | - | Bk247.ACE | Bk247.DIR |
| 371 | 97-Bk-249 | 97249.31c | ptable | Bk249.ACE | Bk249.DIR |
| 372 | 97-Bk-250 | 97250.31c | ptable | Bk250.ACE | Bk250.DIR |
| 373 | 98-Cf-249 | 98249.31c | ptable | Cf249.ACE | Cf249.DIR |
| 374 | 98-Cf-250 | 98250.31c | ptable | Cf250.ACE | Cf250.DIR |
| 375 | 98-Cf-251 | 98251.31c | ptable | Cf251.ACE | Cf251.DIR |
| 376 | 98-Cf-252 | 98252.31c | ptable | Cf252.ACE | Cf252.DIR |
| 377 | 98-Cf-254 | 98254.31c | - | Cf254.ACE | Cf254.DIR |
| 378 | 99-Es-253 | 99253.31c | ptable | Es253.ACE | Es253.DIR |
| 379 | 99-Es-254 | 99254.31c | - | Es254.ACE | Es254.DIR |
| 380 | 99-Es-255 | 99255.31c | - | Es255.ACE | Es255.DIR |
| 381 | 100-Fm-255 | 100255.31c | - | Fm255.ACE | Fm255.DIR |

These libraries were processed at different temperatures: 300, 400, 500, 600, 700, 800, 900, 1000, 1200 and 1800 degrees Kelvin.

Table 2.2. Multi-temperature ACE library

| # | Temperature (K) | ZAID suffix |
| --- | --- | --- |
| 1 | 300 | .31c |
| 2 | 400 | .32c |
| 3 | 500 | .33c |
| 4 | 600 | .34c |
| 5 | 700 | .35c |
| 6 | 800 | .36c |
| 7 | 900 | .37c |
| 8 | 1000 | .38c |
| 9 | 1200 | .39c |
| 10 | 1800 | .40c |

JEFF-3.1 contains some isotopes in ground and isomeric states. These isotopes are processed using the same procedure to obtain .ace and .dir files. However, the ZAID suffix of isomeric states has been changed (+50 to the ground state).

Table 2.3. Isotopes in isomeric state (library at 300K).

| No. | Nuclide | ZAID | PT Tables | ACE filename | XSDIR filename |
| --- | --- | --- | --- | --- | --- |
| 1 | 27-Co – 58M | 27108.31c | - | Co58M.ACE | Co58M.DIR |
| 2 | 47-Ag-110M | 47160.31c | ptable | Ag110M.ACE | Ag110M.DIR |
| 3 | 48-Cd-115M | 48165.31c | - | Cd115M.ACE | Cd115M.DIR |
| 4 | 52-Te-127M | 52177.31c | - | Te127M.ACE | Te127M.DIR |
| 5 | 52-Te-129M | 52179.31c | - | Te129M.ACE | Te129M.DIR |
| 6 | 61-Pm-148M | 61198.31c | - | Pm148M.ACE | Pm148M.DIR |
| 7 | 95-Am-242M | 95292.31c | ptable | Am242M.ACE | Am242M.DIR |
| 8 | 95-Am-244M | 95294.31c | - | Am244M.ACE | Am244M.DIR |

## NJOY inputs to process ACE Thermal Scattering Libraries

Several Scattering Thermal Libraries (STL) have been processed using spetial NJOY inputs. [NDC(NDS)-0470]

Figure 2.3. NJOY input to generate ACE Thermal Scattering library for H bound in CH2.

ACER (thermal scattering libraries)

For hydrogen bound in polyethylene:

| Type of ACER run option | IOPT: | 2 (THERMAL DATA) |
| --- | --- | --- |
| Print control | IPRINT: | 0 (MINIMUN) |
| ACE output type | NTYPE: | 1 |
| ID suffix for ZAID | SUFF: | .31 |
| Material to be processed | MATD: | 125 |
| Temperature desired | NTEMPD: | 293.6K |
| Thermal ZAID name | TNAME: | ‘poly01’ |
| MT for thermal incoherent data* | MTI: | 223 |
| Number of bins for incoherent scattering+ | NBINT: | 64 |
| MT for thermal elastic data* | MTE: | 224 |
| COHERENT/INCOHERENT ELASTIC | IELAS | 0/1 |
| Number of atom types in mixed moderator | NMIX: | 2 |
| Max. energy+ | EMAX: | 4.0 eV |
| Weight option | IWT: | 0/1 VARIABLE/CONSTANT |

* 	MTI and MTE values from Table 3 included in section XVII-22 (ACER module) in NJOY manual.

+ Private communication, M.Mattes, IKE.

Table 2.4. Temperatures for Thermal Scattering Libraries.

To identify these libraries a code is defined for each isotope, see Table 2.5.

To take into account different temperatures in the STLs, the identification code will change according: “lwtrXX.31.t”, where XX=01,02,03, …

Table 2.5. Information on the JEFF-3.1 Thermal Scattering ACE library at 293.6K.

| No. | Nuclide | ZAID | ACE filename | XSDIR filename |
| --- | --- | --- | --- | --- |
| 1 | poly01.31t | Hydrogen bound in polyethylene | H1_H-H2O.ace | H1_H-H2O.dir |
| 2 | lwtr01.31t | Hydrogen bound in water | H1_H-CH2.ace | H1_H-CH2.dir |
| 3 | hzrh01.31t | Hydrogen bound in ZrH | H1_H-ZrH.ace | H1_H-ZrH.dir |
| 4 | grph01.31t | Graphite | C_Graphi.ace | C_Graphi.dir |
| 5 | hwtr01.31t | D bound in D2O | H2_D-D2O.ace | H2_D-D2O.dir |
| 6 | bena01.31t | Be | Be_4-Be-293.6.ace | Be_4-Be-293.6.dir |
| 7 | beo01.31t | Be in BeO | Be_BeO.ace | Be_BeO.dir |

ACER (thermal scattering libraries)

- For hydrogen bound in polyethylene

- For hydrogen bound in water

- For hydrogen bound in ZrH

- Graphite

- For D bound in D2O

- For Be

- For Be in BeO

## QA procedure

### Checking NJOY ouput messages for each material.

The total number of messages was compiled. All messages were understood, most of them are related to incomplete evaluations.

Figure . Example of NJOY messages for Fe56.

- RECONR Output messages

- Message – nonpositive elastic cross section.

Some evaluations uses old single-level Breit-Wigner resonance parameters. This representation occasionally goes negative. NJOY fixes this by setting the cross section to a small positive value.

---message from emerge---nonpositive elastic cross sections found.

Ar40   	     Cd111   	     Cd113   	     Cm244   	     Gd157   	      Ni61   	     Te128         W182

- The initial value of a threshold reaction cross section is different from zero. NJOY has corrected this by using a jump in the cross sectionat the threshold energy.

---message from lunion---xsec nonzero at threshold for mt= XX

F19   	     O16   	     Cl35   	      Cl37   	      Na23   	     Am243   	     Eu155        Nd150   	     Pb204

- This message can be ignored

---message from rdf2bw---calculation of angular distribution not installed

Al27   	      Cr50   	      Cr52   	      Cr53   	      Cr54   	      Cu63   	      Cu65   	      Fe54   	      Fe58   	      I127   	      I129   	      Ni58   	      Ni60   	      Si28   	      Tc99   	     Pb206   	     Pb207   	     Pb208

- HEATR Output messages

- File 12 (multiplicities for photon production) is missing from the ENDF file.

---message from gheat---no file 12 for this material.

N15

---message from h6ddx---vertical segment(s) in distribution

Fe56

- No angular distribution is given for the secondary mt in the evaluation. HEATR assumes isotropic distribution

---message from hinit---mf4 and 6 missing, isotropy assumed for mt =XX

B10   	       N14

- The energy-angle distribution for the specified particle is missing in file 6. NJOY requires energy distributions for all secondary particles from a reaction to compute the energy deposition. In this case, NJOY has to make an assumption and generate an approximate to the data needed.

---message from hinit---mf6, mtXX does not give recoil za=YY

B11   	       Be9   	       Li7   	       N14   	       Tl0   	      Mn55   	      Mo92   	      Mo94   	      Mo95   	      Mo96   	      Mo97   	      Mo98   	      Si29   	      Si30   	      U235   	      W182   	      W183   	      W184   	      W186   	      Zr90   	      Zr91   	      Zr92   	      Zr94   	      Zr96   	     Mo100   	     Np237   	     Sb121   	     Sb123

- In the ENDF format, mt18 (total fission) is the sum of mt19, mt20, mt21 and mt38

---message from hinit---mt18 is redundant

Am242g  	     Cm241   	     Cm244   	     Cm246   	     Pu237   	     Pu244   	     Th232   	      U234

- The partial contribution to the total fission, mt19, has no spectrum. NJOY will use the mt18 spectrum

---message from hinit---mt19 has no spectrum

U235   	      U236   	      U237   	      U238

- No partial components of the fission energy released are given in the evaluation

---message from hinit---mt458 is missing for this mat

Ac227   	    Am242g   	     Am244   	    Am244m   	     Bk247   	     Bk249   	     Bk250   	     Cf249   	     Cf250   	     Cf251   	     Cf252   	     Cf254   	     Cm240   	     Cm245   	     Cm246   	     Cm247   	     Cm249   	     Cm250   	     Es254   	     ES255   	     Fm255   	     Np235   	     Np236   	     Np238   	     Np239   	     Pa231   	     Pa232   	     Pu243   	     Pu246   	     Ra223   	     Ra226   	     Th227   	     Th228   	     Th229   	     Th233   	     Th234   	      U232   	      U237

- NJOY does not include energy from delayed emission in the prompt heating. The fission Q-value is changed from the total value given in file 3 to a prompt value using the delayed neutron energy from mf1, mt458.

---message from nheat---changed q from   E1 to   E2

U233   	      U234   	      U235   	      U236   	      U238   	     Am241   	     Am243   	     Cm241   	     Cm242   	     Cm243   	     Cm244   	     Cm248   	     Np237   	     Pa233   	     Pu236   	     Pu237   	     Pu238   	     Pu239   	     Pu240   	     Pu241   	     Pu242   	     Pu244   	     Th230   	     Th232   	     Th232   	    Am242m

- The ENDF6 format allows an evaluator to describe a subsection of file 6 using LAW=0 (no distribution given). This is fine for particle yields for gas production, . . . but they are not adequate for computing heating and damage.

---message from sixbar---no distribution for mt  5 particle **

Bi209   	      Ca40   	      Ca42   	      Ca43   	      Ca44   	      Ca46   	      Ca48   	      Fe54   	      Fe56   	      Fe57   	      Fe58   	      Ge70   	      Ge72   	      Ge73   	      Ge74   	      Ge76   	     Pb204   	     Pb206   	     Pb207   	     Pb208   	      Sc45   	      Tc99

- PURR Output messages

- When a material has no resonance parameters associated with it, this message will be issued.

---message from purr---mat 8925 has no resonance parameters

Ac225	Ac226	Ac227	Ag111	Am244	Am244m	B10	B11	Be9	C0	Ca46	Cd115M	Ce143	Cf254	Cl35	Cl37	Cm241	Es254	ES255	Eu156	Eu157	F19	Fm255	H1	H2	H3	He3	He4	Hg204	I130	I131	I135	K40	Kr85	La140	Li6	Li7	N14	N15	Np235	Np236	Np239	O16	O17	Pm148	Pm149	Pm151	Pr142	Pr143	Pt0	Pu237	Pu246	Ra223	Ra224	Ra225	Rb86	Rh105	Ru105	Ru106	Ru96	Ru98	S36	Sb124	Sb125	Sb126	Sm144	Sm148	Sm153	Sn123	Sn125	Sn126	Sr89	Sr90	Tb160	Te120	Te127M	Te129M	Te132	Th227	Th233	Th234	Ti46	Ti47	Ti48	Ti49	Ti50	Xe133	Xe135	Xe136	Y90	Y91

- The entire resolved energy range seems to overlap the unresolved energy range for this material. NJOY deals with this but no probability tables will be generated by purr as there won't be any unresolved resonance parameters left (they are removed from the file). Another possibility is that the material has no unresolved resonances and that purr was run.

---message from purr---mat 4725 has no unresolved parameters

Ag107	Al27	Ar40	As75	Au197	Ba138	Bi209	Bk247	Br79	Br81	Ca40	Ca42	Ca43	Ca44	Ca48	Cd111	Cd113	Ce140	Co58	Co58M	Co59	Cr50	Cr52	Cr53	Cr54	Cs134	Cs136	Cu63	Cu65	Dy160	Dy163	Er162	Er164	Er166	Er168	Er170	Fe54	Fe56	Fe57	Ga0	Gd154	Gd157	Gd158	Gd160	Ge70	Ge72	Ge73	Ge74	Ge76	Hg196	Hg198	Hg199	Hg200	Hg201	Hg202	Ho165	K39	K41	Kr78	Kr80	Kr82	Kr83	Kr84	Kr86	Mg24	Mg25	Mg26	Mn55	Na23	Nb93	Nd142	Nd147	Nd150	Ni58	Ni59	Ni60	Ni61	Ni62	Ni64	Os0	P31	Pa232	Pb204	Pb206	Pb207	Pb208	Pd102	Pm148M	Ra226	Rb85	Rb87	Ru100	Ru102	Ru104	Ru99	S32	S33	S34	Sc45	Se74	Se76	Se77	Se78	Se80	Se82	Si28	Si29	Si30	Sm150	Sm154	Sr84	Sr86	Sr87	Sr88	Te122	Te123	Te124	Te125	Te126	Te128	Te130	Th228	Th229	Th230	Tl0	U236	V0	W182	W183	W184	W186	Xe124	Xe126	Xe128	Xe129	Xe130	Xe131	Xe132	Xe134	Y89	Zn0	Zr90	Zr96

- ACER Output messages

- The second acer run provides a consistency check of the ACE file produced by the first acer run. Whenever something abnormal is found, this message will be printed.

---message from consis---consistency problems found

Al27   	       Be9   	     Bi209   	        C0   	      Ca40   	      Ca42   	      Ca43   	      Ca44   	      Ca46   	      Ca48   	      Cu63   	      Cu65   	      Fe54   	      Fe56   	      Fe57   	      Fe58   	      Ge70   	      Ge72   	      Ge73   	      Ge74   	      Ge76   	      I127   	      I129   	     Mo100   	      Mo95   	      Mo97   	       N14   	      Na23   	      Nb93   	      Ni61   	      Ni62   	      Ni64   	       O16   	       P31   	     Pb204   	     Pb206   	     Pb207   	     Pb208   	     Pu239   	     Rh103   	     Sb121   	     Sb123   	      Sc45   	      Si29   	      Si30   	      Tc99   	      U233   	      U235   	      W182   	      W183   	      W184   	      W186   	      Zr96

- This message indicates that a negative PDF value was found, NJOY sets the value to zero and renormalizes the distribution

---message from ptleg2---negative probs found

B10   	       B11   	      Co58   	      U232   	      U233   	      U235   	     Ac225   	     Ac227   	     Ag109   	     Am244   	     Au197   	     Bk250   	     Cf254   	     Cm240   	     Cm242   	     Cm243   	     Cm245   	     Cm247   	     Cm248   	     Er166   	     Er167   	     Er168   	     Er170   	     Es254   	     ES255   	     Fm255   	     Hf177   	     Hf179   	     Hg196   	     Hg198   	     Ho165   	     La139   	     Pa231   	     Pd106   	     Pd107   	     Pd108   	     Pd110   	     Pu238   	     Pu244   	     Pu246   	     Ra223   	     Ra224   	     Ra225   	     Ra226   	     Ru101   	     Sm151   	     Th229   	     Th230   	    Am244m

- The ptleg subroutine of the acer module translates ENDF Legendre angular distributions into tabulated form with equal probability m intervals. In this routine the cosine interval m= -1 to 1 is divided into 1000 intervals and integrated. When the integral of the angular distribution over such an interval is negative, we receive this message. This is caused by the fact that the Legendre polynomial series can lead to negative values.

---message from ptleg---negative area between mu= XX and YY

O16

- This error normally surfaces when there is an inconsistency between the threshold energy of a reaction in the ENDF file and the value calculated by NJOY. This is already checked and corrected in reconr so this error should never occur. However, NJOY uses ENDF files to transfer information between modules in which any number is rounded to 6 significant digits. In the case of the above mentioned nuclides, the difference between the calculated value and the one in the ENDF file occurs in the 7th significant digit (which is lost due to rounding).

---message from unionx---threshold error

Be9       P31

### Checking ACE libraries

During the processing of ENDF60 [ENDF60] and ENDF66 [LA-UR-03-0954] standard ACE libraries several test were performed using external codes. Some of them have already been added to the internal NJOY testing in RECONR and ACER modules.

The second ACE pass performs ACE consistency, checks and corrects problems that might be detected. In fact, the main questions performed by ACER are [ALEPH-DLG, LA-UR-98-5718]:

  - Do threshold values correspond to Q-values?

- Checked by RECONR

  - Is the energy grid monotonically increasing?

- Checked by RECONR (the unionized grid is assumed monotonic). If two points with the same energy are found (i.e.: a jump in the cross section), a consistency problem is signalled but this can be ignored.

  - Check the angular distributions for the correct reference frame (either CM or LAB)

  - Check the angular distributions for unreasonable cosines

  - Is the emission energy less than the incident energy?

  - Do summation cross sections match sums?

- Checked by RECONR

  - Ensure that probability density functions are non-negative

- Checked by ACER

  - Are only appropriate interpolation values used?

  - Do threshold reactions start with a zero cross section?

- Checked by RECONR

Table 2.6. NJOY output showing several consistency checks

In the last section we found consistency problems for many materials, see Table 2.7.

Table 2.7. Output messages in 2nd ACER

| Al27 | check energy distributions consis: ep.gt.epmax 9.292258E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| --- | --- |
| Be9 |  |
| Bi209 | check energy distributions consis: ep.gt.epmax 9.904161E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.ge.180---there could be a legitimate positive-q channel or admixed fission. |
| C0 | check energy distributions consis: ep.gt.epmax 8.509482E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca40 | check energy distributions consis: ep.gt.epmax 9.513683E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca42 | check energy distributions consis: ep.gt.epmax 9.536006E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca43 | check energy distributions consis: ep.gt.epmax 9.546438E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca44 | check energy distributions consis: ep.gt.epmax 9.556378E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca46 | check energy distributions consis: ep.gt.epmax 9.575049E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ca48 | check energy distributions consis: ep.gt.epmax 9.592217E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Cu63 | check energy distributions consis: ep.gt.epmax 9.686976E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Cu65 | check energy distributions consis: ep.gt.epmax 9.696388E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Fe54 | check energy distributions consis: ep.gt.epmax 9.636236E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Fe56 | check energy distributions consis: ep.gt.epmax 9.648868E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Fe57 | check energy distributions consis: ep.gt.epmax 9.654878E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |

| Fe58 | check energy distributions consis: ep.gt.epmax 9.660670E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| --- | --- |
| Ge70 | check energy distributions consis: ep.gt.epmax 9.717621E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ge72 | check energy distributions consis: ep.gt.epmax 9.725303E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ge73 | check energy distributions consis: ep.gt.epmax 9.728998E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ge74 | check energy distributions consis: ep.gt.epmax 9.732582E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ge76 | check energy distributions consis: ep.gt.epmax 9.739489E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| I127 |  |
| I129 | check energy distributions consis: ep.gt.epmax 9.845319E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Mo100 | check that main energy grid is monotonic consis: energy 4.20000100E-01 less than 4.20000100E-01 (see point no. 26576) checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.700000E+01 -> 1.101400E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.900000E+01 -> 9.677970E+00 |
| Mo95 | check photon production sum consis: mismatch at 1.000001E-03 gpd= 1.039925E-01 sum= 1.040143E-01 checking particle production sections alpha production: checking energy distributions consis: bad law61 cumm. prob for (n,a*c) at 1.000000E-11 -> 4.154300E+00 consis: decreasing law61 cumm. prob for (n,a*c) at 1.000000E-11 -> 4.154300E+00 consis: bad law61 cumm. prob for (n,a*c) at 1.000000E-03 -> 4.154300E+00 consis: decreasing law61 cumm. prob for (n,a*c) at 1.000000E-03 -> 4.154300E+00 |
| Mo97 | check that main energy grid is monotonic consis: energy 4.20000100E-01 less than 4.20000100E-01 (see point no. 13003) checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.800000E+01 -> 1.573730E+01 |
| N14 | check energy distributions consis: ep.gt.epmax 8.701311E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |

| Na23 | check angular distributions for correct reference frame consis: should be lab: (n,n*c) |
| --- | --- |
| Nb93 | check energy distributions consis: ep.gt.epmax 9.786342E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ni61 | check energy distributions consis: ep.gt.epmax 9.676960E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ni62 | check energy distributions consis: ep.gt.epmax 9.682034E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Ni64 | check energy distributions consis: ep.gt.epmax 9.691751E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| O16 | check energy distributions consis: ep.gt.epmax 8.848774E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-11 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| P31 | check reaction thresholds against q values consis: threshold 3.40230200E+00 less than the expected 3.40230208E+00 for (n,n*4) |
| Pb204 | check energy distributions consis: ep.gt.epmax 9.901826E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.ge.180---there could be a legitimate positive-q channel or admixed fission. |
| Pb206 |  |
| Pb207 | check energy distributions consis: ep.gt.epmax 9.903240E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.ge.180---there could be a legitimate positive-q channel or admixed fission. |
| Pb208 | check energy distributions consis: ep.gt.epmax 9.903702E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.ge.180---there could be a legitimate positive-q channel or admixed fission. |
| Pu239 | check angular distributions for correct reference frame consis: should be lab: (n,n*c) check delayed neutron fraction consis: delayed fractions do not sum to one |
| Rh103 |  |
| Sb121 | checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.600000E+01 -> 1.512400E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.300000E+01 -> 7.130260E+00 triton production: checking energy distributions consis: bad law44 kalbach r for (n,xt) at 1.800000E+01 -> 9.996470E+00 |
| Sb123 | checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.800000E+01 -> 1.512600E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.500000E+01 -> 1.008340E+01 triton production: checking energy distributions |
| Sc45 | check energy distributions consis: ep.gt.epmax 9.565927E-12 with q.lt.0 for (n,x) at e 1.000000E-11 -> 1.000000E-06 consis: awr.lt.180---this is probably an error. consis: shifting eprimes greater than epmax and renorming the distribution |
| Si29 | check that main energy grid is monotonic consis: energy 7.30265100E+00 less than 7.30265100E+00 (see point no. 1407) |
| Si30 | check that main energy grid is monotonic consis: energy 7.23453100E+00 less than 7.23453100E+00 (see point no. 2075) |
| Tc99 |  |
| U233 | check that main energy grid is monotonic consis: energy 1.09000100E+00 less than 1.09000100E+00 (see point no. 9344) check delayed neutron fractions consis: delayed fractions do not sum to one |
| U235 | check delayed neutron fractions consis: delayed fractions do not sum to one |
| W182 | check that main energy grid is monotonic consis: energy 4.00000100E-01 less than 4.00000100E-01 (see point no. 33722) checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.500000E+01 -> 1.317710E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.800000E+01 -> 1.063170E+01 alpha production: checking energy distributions consis: bad law44 kalbach r for (n,xa) at 1.900000E+01 -> 2.616490E+01 |
| W183 | check that main energy grid is monotonic consis: energy 1.00000100E-01 less than 1.00000100E-01 (see point no. 21588) checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.500000E+01 -> 1.317740E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.500000E+01 -> 9.643280E+00 alpha production: checking energy distributions consis: bad law44 kalbach r for (n,xa) at 1.600000E+01 -> 2.372250E+01 |
| W184 | check that main energy grid is monotonic consis: energy 4.00000100E-01 less than 4.00000100E-01 (see point no. 28845) checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.600000E+01 -> 1.268060E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.800000E+01 -> 1.063300E+01 alpha production: checking energy distributions consis: bad law44 kalbach r for (n,xa) at 1.800000E+01 -> 2.372540E+01 |
| W186 | checking particle production sections proton production: checking energy distributions consis: bad law44 kalbach r for (n,xp) at 1.700000E+01 -> 1.268130E+01 deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.400000E+01 -> 7.666530E+00 alpha production: checking energy distributions consis: bad law44 kalbach r for (n,xa) at 1.900000E+01 -> 2.324170E+01 |
| Zr96 | checking particle production sections deuteron production: checking energy distributions consis: bad law44 kalbach r for (n,xd) at 1.800000E+01 -> 6.609760E+00 |

However, ACER does not include the capability to checks the proper processing of the unresolved resonance probability tables.

The Probability table (PT) method was implemented in MCNP to account statistically for the average resonance parameters specified in the unresolved resonance range. In this method, the average parameters are used to generate ladders of representative resonances.

Cross sections from these ladders are the used to form cross-section probability distribution functions, from which a table of cross sections (total, elastic, fission, and radiative capture) as a function of probability is prepared. MCNP samples the total and reaction cross sections at the energy of the neutron, rather than simply using single average values at this energy.

These PTs are calculated in PURR module. And sigma zero values are not required and could be omitted entirely if the only objective is to generate an ACE library.

Verification of URES library can be performed with a variety of consistency test on the PT data: [LA-UR-98-5718]

- Ensure that any competition reaction specified actually exists

- Check the infinitely-dilute total cross section at the energy of the PT against the sum of the infinitely-dilute elastic, fission, capture and competition cross sections.

- Make sure that the cumulative probabilities as given in the PT are in ascending order, and that the distribution is correctly normalized to 1.

- Check negative values of the total, elastic, fission and capture cross sections in each row of the PT. In addition, checks for zero cross sections for the total, elastic and capture.

- Check for zero or negative values of the heating numbers in each row of the PT

- Compare the total cross section from the PT with the sum of the elastic, fission, capture and competition process.

- For each cross section, compare the infinitely dilute value at that neutron energy with the apparent average value from the PT.

The ENDF/B-VI evaluators decided to drop plans to include data for any isotope with a large number of negative cross sections in the PT data. The problems were traced to negative background cross sections in ENDF libraries. (Report LA-UR-03-594). So the negative cross section problems in the PT are related with the evaluation and it is not a problems with the purr module of NJOY ( the method of calculating the probability table as implemented in NJOY should not lead negative values by itself [ALEPH-DLG])

In short, there are a number of possible problems or abnormalities with the PTs that can be directly noticed for some isotopes:

- Probability bins with a probability of 0, these bins will not be sampled so it can be accepted

- Zero cross section values (either for the entire bin or for specific reactions)

- Negative cross section values

Zero cross sections can occur either in the lower bins because the cross section becomes very small or when the particular row has a fractional probability of zero (in this case, the row will never be sampled). In these cases, zero cross section can be allowed.

Negative cross sections however cannot be allowed (and the library file has to be recalculated without probability tables), unless they appear in a row with zero fractional probability (in which case they will not be used).

The procedure in this work is to simply omit the PT from ACE file whenever negative values are found.

Negative cross section values for capture PT can be found( see Table 2.8).

Table 2.8. Probability table for Ag-109 at E=9.840E+02 eV.

### Q&A with ACELST code

Our objective in this section is to show the results applied to JEFF-3.1 library using the QA procedure developed by D. López Aldama and A. Trkov in ADS-Lib/V1.0. Here, “the human eye will be used as a wonderfully complex tool, able to spot inconsistency and error with amazing precision”[LA-UR-02-1235]:

- Look for unexpected discontinuities in cross sections

- Examine secondary distributions

- Examine threshold regions

- Examine resonance regions

For all the ACE-formatted files, we have converted back to ENDF-6 format using the code ACELST[ACELST]. These ENDF6 files were compared with the original evaluation using different procedures:

- Using NJOY code

- Using PREPRO-2004 code system (LINEAR + RECENT + SIGMA1) [PREPRO2004]

We can conclude that the processed data were judged to be acceptable:

- Differences between NJOY and PREPRO2004 should be investigated

- Differences with other libraries should be considered for later validations.

### Example of Q&A with ACELST code: Fe56

- Comparison ACE result with original ENDF

NJOY99 code is used to compare original ENDF library with the processed library in ACE format converted-back into ENDF format using ACLST code.

Figure 2.4. Comparison of the capture cross section processed by NJOY in PENDF format: original ENDF versus ACE library processed by ACELST

In conclusion: no deviations in the cross section data were found.

- Comparison JEFF-3.1 with ENDF/B-VI.R8 processed by NJOY code

Figure 2.5. Comparison of the Fe-56 cross sections processed by NJOY in PENDF format: ENDF/B-VI.R8 versus JEFF-3.1.

Figure 2.5. Comparison of the Fe-57 cross sections processed by NJOY in PENDF format: ENDF/B-VI.R8 versus JEFF-3.1.

- Comparison: PREPRO-2004 versus NJOY99

ACEQA code developed by D.L. Aldama compare PREPRO-2004 (LINEAR+RECENT+SIGMA1) and NJOY cross sections in PENDF format.

Figure 2.6. Comparison of the capture cross section processed by NJOY and PREPRO2004 code.

- PREPRO-2004 Warnings and messages were also compiled

In order to compare PREPRO-2004 and NJOY99, ACEQA code runs LINEAR+RECENT+SIGMA1 codes consecutively.

Warnings and messages from these codes are useful to complete an additional check.

Table 2.9. Example of RECENT.LST messages/warnings for 56Fe and 57Fe.

| Nuclide | Codes | Warnings |
| --- | --- | --- |
| 26-Fe- 56 | LINEAR | None |
|  | RECENT | WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING L Dependent Scattering Radius in the Evaluation is Zero. Have Defined it to be Equal to the Scattering Radius .544400000 (see, ENDF/B-VI Formats and Procedures Manual, page 2.11) WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING L Dependent Scattering Radius in the Evaluation is Zero. Have Defined it to be Equal to the Scattering Radius .544400000 (see, ENDF/B-VI Formats and Procedures Manual, page 2.11) |
|  | SIGMA1 | None |
| 26-Fe- 57 | LINEAR | None |
|  | RECENT | WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING L Dependent Scattering Radius in the Evaluation is Zero. Have Defined it to be Equal to the Scattering Radius .650000000 (see, ENDF/B-VI Formats and Procedures Manual, page 2.11) WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING L Dependent Scattering Radius in the Evaluation is Zero. Have Defined it to be Equal to the Scattering Radius .650000000 (see, ENDF/B-VI Formats and Procedures Manual, page 2.11) ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING L= 1 J = 1.000 Corresponds to 2 Resonance Sequences. ------------------------------------------------------------------------------ ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING FOR L = 1 Expect Sum of Statistical Weights (GJ) to Equal (2*L + 1) = 3.000 Found = 2.250 Corrective Action Will be Taken to Correctly Calculate the Potential Scattering Cross Section - This Procedure is Based on the Decision of the National Nuclear Data Center, Brookhaven National Laboratory, Private Communication, Charles Dunford, (April 1991) |
|  | SIGMA1 | None |

For many materials warnings/messages are obtained when running  LINEAR-RECENT-SIGMA1 codes. Only materials with SIGMA1 warnings are shown in Table 2.10.

Table 2.10. List of warnings for JEFF-3.1 library processed with LINEAR-RECENT-SIGMA1 codes. Only materials with SIGMA1 warnings are shown.

| Nuclide | Codes | Warnings |
| --- | --- | --- |
| 22-Ti- 46 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 22-Ti-46 2225 3 2 VI 0.0 0.0 4604 4604 WARNING - Above Cross Section Negative at 11 Energies |
|  | RECENT |  |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 22-Ti-46 2225 2 VI 0.0 0.0 4604 8335 WARNING - Above Cross Section Negative at 23 Energies |
| 22-Ti- 49 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 22-Ti-49 2234 3 2 VI 0.0 0.0 5140 5140 WARNING - Above Cross Section Negative at 7 Energies |
|  | RECENT |  |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 22-Ti-49 2234 2 VI 0.0 0.0 5140 8282 WARNING - Above Cross Section Negative at 8 Energies |
| 22-Ti- 50 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 22-Ti-50 2237 3 2 VI 0.0 0.0 4577 4577 WARNING - Above Cross Section Negative at 7 Energies |
|  | RECENT |  |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 22-Ti-50 2237 2 VI 0.0 0.0 4577 8301 WARNING - Above Cross Section Negative at 10 Energies |
| 27-Co- 58 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 27-Co-58 2722 3 1 VI 0.0 0.0 422 422 WARNING - Above Cross Section Negative at 52 Energies 27-Co-58 2722 3 2 VI 0.0 0.0 326 326 WARNING - Above Cross Section Negative at 249 Energies |
|  | RECENT | ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING for L= 0 The Following J Sequences are Missing. J = 2.50 ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING FOR L = 0 Expect Sum of Statistical Weights (GJ) to Equal (2*L + 1) = 1.000 Found = 0.400 Corrective Action Will be Taken to Correctly Calculate the Potential Scattering Cross Section - This Procedure is Based on the Decision of the National Nuclear Data Center, Brookhaven National Laboratory, Private Communication, Charles Dunford, (April 1991) Capture 655 404 1041 WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING Above Cross Section is Negative at 109 Energies. |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 27-Co-58 2722 102 VI 0.0 10450000.0 1041 831 WARNING - Above Cross Section Negative at 217 Energies |
| 52-Te-128 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 52-Te-128 5249 3 1 VI 0.0 0.0 612 620 WARNING - Above Cross Section Negative at 185 Energies 52-Te-128 5249 3 2 VI 0.0 0.0 541 558 WARNING - Above Cross Section Negative at 186 Energies |
|  | RECENT | ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING for L= 1 The Following J Sequences are Missing. J = 1.50 ------------------------------------------------------------------------------ WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING FOR L = 1 Expect Sum of Statistical Weights (GJ) to Equal (2*L + 1) = 3.000 Found = 1.000 Corrective Action Will be Taken to Correctly Calculate the Potential Scattering Cross Section - This Procedure is Based on the Decision of the National Nuclear Data Center, Brookhaven National Laboratory, Private Communication, Charles Dunford, (April 1991) … … Total 16011 620 16608 WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING Above Cross Section is Negative at 485 Energies. Elastic 16011 558 16546 WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING Above Cross Section is Negative at 714 Energies. |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 52-Te-128 5249 1 VI 0.0 0.0 16608 4075 WARNING - Above Cross Section Negative at 673 Energies n 52-Te-128 5249 2 VI 0.0 0.0 16546 3849 WARNING - Above Cross Section Negative at 745 Energies |
| 64-Gd-157 | LINEAR | ------------------------------------------------------------------------------ Material MAT MF MT ENDF/B Kelvin Q-Value Points Points Format eV In Out ------------------------------------------------------------------------------ 64-Gd-157 6440 3 1 VI 0.0 0.0 645 685 WARNING - Above Cross Section Negative at 251 Energies 64-Gd-157 6440 3 2 VI 0.0 0.0 637 669 WARNING - Above Cross Section Negative at 250 Energies |
|  | RECENT | Elastic 13220 669 13870 WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING...WARNING Above Cross Section is Negative at 229 Energies. |
|  | SIGMA1 | ------------------------------------------------------------------------------ Projectile MAT MT ENDF/B Kelvin Q-Value Points Points Material Format In eV In Out ------------------------------------------------------------------------------- n 64-Gd-157 6440 2 VI 0.0 0.0 13870 5321 WARNING - Above Cross Section Negative at 312 Energies |

## Differences: PREPRO-2004 versus NJOY99

The parameters used to run PREPRO-2004 in LINEAR, RECENT and SIGMA1:

***************** Program LINEAR (VERSION 2004-1) ***************

For All Data Greater than 1.0000E-10 barns in Absolute Value

Data Linearized to Within an Accuracy of .100000000 per-cent

***************** Program RECENT (VERSION 2005-1) ***************

for All Data Greater than 1.0000E-10 barns in Absolute Value

Data Linearized to within an Accuracy of .100000000 per-cent

***************** Program SIGMA1 (VERSION 2005-1) ***************

Data Doppler Broadened to 300.000000 Kelvin

for All Data Greater than 1.0000E-10 barns in Absolute Value

Data Linearized to Within an Accuracy of .100000000 per-cent

In this section NJOY99 means cross sections converted-back from ACE format using ACELST code. Consequently, their accuracy options are the options used in processing ACE files.

### Case Tl0.nat

Inconsitency found at low neutron thermal energy: it is due to the type of interpolation low used at low energy.

In the cross section library, JEFF-3.1 uses a lin-lin interpolation at low energy.

Table 2.11. MT=102 for Tl0 material taken from JEFF-3.1

However, SIGMA1 code changes the interpolation law according to the sentences in Table 2.12.

Table 2.12. SIGMA1 code used to interpolation at low energy.

Figure 2.7. Differences in Tl-nat  capture cross section

### Total cross sections

Differences in the total cross sections are due to:

- NJOY code calculates the total cross section summing the partial cross sections

- PREPRO-2004 processes directly the section MT=1, MF=3.

Figure 2.8. Total cross section for O-17 processed by PREPRO-2004 and NJOY99.

Figure 2.9. Total cross section for I-135 processed by PREPRO-2004 and NJOY99.

Figure 2.10. Total cross section for Th-232 processed by PREPRO-2004 and NJOY99.

Figure 2.11. Total cross section for Ho-165 processed by PREPRO-2004 and NJOY99.

### Resonances

Figure 2.12. Elastic cross section for Cm-249 processed by PREPRO-2004 and NJOY99.

Figure 2.13. Capture cross section for Ag-110M processed by PREPRO-2004 and NJOY99.

Figure 2.14. Elastic cross section for Co-59 processed by PREPRO-2004 and NJOY99.

Figure 2.15. Capture cross section for Nb-95 processed by PREPRO-2004 and NJOY99.

Figure 2.16. Elastic cross section for Ni-58 processed by PREPRO-2004 and NJOY99.

Figure 2.17. Capture cross section for Ti-47 processed by PREPRO-2004 and NJOY99.

Figure 2.18. Elastic cross section for Cm-244 processed by PREPRO-2004 and NJOY99.

Figure 2.19. Elastic cross section for Fe-57 processed by PREPRO-2004 and NJOY99.

Figure 2.20. Capture cross section for Fe-57 processed by PREPRO-2004 and NJOY99.

Figure 2.21. Elastic cross section for Ni-60 processed by PREPRO-2004 and NJOY99.

Figure 2.22. Elastic cross section for Ni-61 processed by PREPRO-2004 and NJOY99.

Figure 2.23. Elastic cross section for Pb-206 processed by PREPRO-2004 and NJOY99.

Figure 2.24. Capture cross section for S-32 processed by PREPRO-2004 and NJOY99.

Figure 2.25. Capture cross section for Sc-45 processed by PREPRO-2004 and NJOY99.

Figure 2.26. Elastic cross section for Te-128 processed by PREPRO-2004 and NJOY99.

Figure 2.27. Capture cross section for Ti-46 processed by PREPRO-2004 and NJOY99.

### Case: Co58

The resonance goes to 0.0 in the resonance capture cross section.

The reason of this problem is due to negative cross section in MT102 and the combination of a single-level Breit Wigner resonance file.

Figure 2.28. Capture cross section for Co-58 processed by PREPRO-2004 and NJOY99.

# NJOY99.90 + updates to process ACE library.

Several Research Centers have developed specific NJOY99.90 updates to be used in nuclear data processing. An intensive work has been performed in order to compile the most recent NJOY90.90 updates to process the JEFF-3.1 library. [NJOY99_up90, NJOY99_up112]

## NJOY99.90

First, the NJOY99.90 was used to process the JEFF-3.1library. Problems with some isotopes were found in NJOY modules (the NJOY patches able to deal with these problems are identified):

- ACER:  	Al-27, Cl-35, I-129, Rh-103 (upn_Cabellos)

- PURR: 	Es-253 (upn_Pescarini)

- HEATR: 	Eu-151 (upn_Pescarini)

- HETAR: 	Mo-95 (upn_Pescarini and upn_Cabellos)

- GASPR:    	I-127, Ni-58, Pb-206, Tc-99, Zn0 (upn_Pescarini or upn_Trkov/Aldama)

## NJOY99.90+NEA updates

We have considered the most recent NJOY corrections developed by:

- D. Leichtle, I. Schmuck (FZK)

allow for processing of EFF3.0/NMOD=3 9Be with (n,2n) subsections in MT875-890

- D. L. Aldama, NDS/IAEA Consultant, July 2005

Included in ADS-lib/V1.0

- O. Cabellos, NEA Data Bank Consultant, Sep-2005

- A. Hogenbirk (NRG), 21sep2001

NRG updates for ACER-processing of delayed neutron data

- M. Mattes/IKE

Thermal scattering cross sections

- M. Pescarini

Updates for JEFF-3.1

- Kazuaki Kosako, Shimizu Corporation

- J.C. Sublet, Feb. 2005

- A.Trkov, IAEA

IAEA updates, FENDL updates, WLUP updates

We have processed these updates, and we have obtained a unique update to be used in this work. To reach this objective an extensive work has been performed:

- checking consistency between different updates

- correcting small bugs

A comparison with the most recent NJOY update, upn112 will be shown in section 3.2.

Figure 3.1. Build NJOY using some NJOY patches

## NJOY99.112+JEFF3.1-updates

To process the JEFF-3.1 library with the recent updated released by McFarlane (upn112) we have to include two additional updates:

- The Pescarini’s patch

*/ --------- correction in heatr/gambar (case Eu-151)

*d heatr.4845

*/ -------- correction in thermr/coh (Be_TH,C_GPH cases)

*i thermr.782

*/ -------- correction in purr/rdf3un (case Es-253)

*i purr.978

- The Cabellos’ patch

*/ Error when processing Al-27, Cl-35,I-129,Rh-103

*/ in acer

*/ Error when processing Thermal Scattering for H-1(in H2O) at */ 293.6K (llf=0)

*/ in broadr

Table 3.1 . Procedure to obtain NJOY source to process JEFF-3.1 library

In addition, we have compared this upn112 patch with NJOY updates considered in section 3.1. Most of the previous updates are included in upn112, except for:

- The delayed neutron processing by Hogenbirk (FZK). Patch upn112 includes a simplified correction in up96.

*/ acer -- 21sep2001 A. Hogenbirk (NRG)

*/ -----------------------------------------------

*/          allow processing of delayed nu data

*/          for use in MCNP (version 4C onwards)

*/ -----------------------------------------------

- The Be9(n,2n) processing by D. Leichtle & I. Schmuck (FZK)

*/ corrections by D. Leichtle, I. Schmuck (FZK)

*/ allow for processing of EFF3.0/NMOD=3 9Be with (n,2n)

*/ subsections in MT875-890 in ACER.

- The upn_Shimizu.

*/ Kazuaki Kosako, Shimizu Corporation

*/ MF5 and MF6 INT=21-25 laws modifications

*/ in groupr

*/ Kazuaki Kosako, Shimizu Corporation

*/ kinematic meted

*/ in heatr

This upn112 includes the rest of corrections previously considered in section 3.1. Some additional small corrections are also incorporated in upn112.

# Conversion of the library: makxsf

The program makxsf from the MCNP-4C package is used for ASCII to BCD conversion of the library. It can also be used to organize data tables for building cross-section libraries.

Three inputs are required for makxsf:

- Nuclear data tables/cross-section libraries

- A data directory file (xsdir)

- The file specs (specs)

Figure 3.2. Input/Output  for makxsf

Figure 3.3 . Procedure to make xsdir file: “run_xsdir.bat”

Figure 3.4. File “specs_type1”. It describes how the new library will be generated (jeff31_ascii).

Figure 3.5. File “xsdir_type1 ”.  This file contains the header of the classical xsdir file (datapath, atomic weight ratios and directory sections).

The data directory file consists of three sections:

- Optional line that specifies the path where the cross-section data are located

- Atomic weight ratios

- Descriptions of the data tables that form the library. This directory section is completed by adding the .dir  file for each material processed.

Figure 3.6. File “specs_type2”. To convert the ASCII library (jeff31_ascii) into Binary (jeff31_bin).

# Validation

## Criticality Validation

An extensive criticality validation suite can be used by the International Handbook of Evaluated Criticality Safety Benchmark Experiments from the OECD-NEA project ICSBEP [ICSBEP].

It contains cases for a variety of fuels, including:

- 233U

- highly enriched uranium (HEU)

- intermediate-enriched uranium (IEU)

- low-enriched uranium (LEU)

- plutonium

For each type of fuel, there are cases with a variety of:

- moderators

- reflectors

- spectra

- geometries

Two suites of calculations were performed:

- A Validation Suite proposed by LANL (Russel D. Mosteller)

- An additional validation, also included in ICSBEP for:

  - Np237

  - heavy-Water solutions

  - very thermal Pu solution

  - unmoderated ZEUS benchmark

Other references have been used to compare these calculations [ALEPH-DLG , JEFDOC-1107].

### LANL Validation Suite

A MCNP criticality validation suite has been recently proposed by R.D. Mosteller (LANL) to assess the reactivity impact of improvements to MCNP as well as changes to associated nuclear data libraries [LA-UR-05-8430]. This suite is a collection of 31 benchmarks taken from the International Handbook of Evaluated Criticality Benchmark Experiments (see Table 1). It contains:

- Fuels:

  - 233U

  - 239Pu

  - 235U:

    - highly enriched uranium (HEU)

    - intermediate-enriched uranium (IEU)

    - low-enriched uranium (LEU)

- For each fuel type, there are cases with a variety of:

  - Spectra: Fast, intermediate  and thermal

  - Compositions: Metals, oxides and solutions

  - Configurations: Bare and reflected spheres and cylinders, 2-D and 3-D lattices, infinite homogeneous and heterogeneous regions.

Table 4.1. MCNP Criticality Validation Suite proposed by R.D. Mosteller, LANL.

| Spectrum | Fast | Intemediate | Thermal |
| --- | --- | --- | --- |
| Geometry | Bare | Heavy reflector | Light reflector | Any | Lattice of fuel Pins in water | Solution |
| 233U | Jezebel-233 | Flattop-23 | U233-MF-05 (2)* | Falstaff (1)+ | SB-2½ | ORNL-11 |
| HEU | Godiva Tinkertoy-2 (c11) | Flattop-25 | Godiver | UH3 (6) Zeus (2) | SB-5 | ORNL-10 |
| IEU | IEU-MF-03 | BIG TEN | IEU-MF-04 | Zebra-8H# | IEU-CT-02 (3) | STACY-36 |
| LEU |  |  |  |  | BaW XI (2) | LEU-ST-02 |
| Pu | Jezebel Jezebel-240 Pu Buttons (3) | Flattop-Pu THOR | Pu-MF-11 | HISS/HPG | PNL-33 | PNL-2 |

* 	Numbers in parenthesis identify a specific case within a sequence of benchmarks

+ 	Extrapolated to critical

# 	k∞ measurements

The MCNP5 calculations were run with 5,000,000 active neutron histories for all but two cases in the suite (550 generations with 10,000 neutrons per generation, excluding the first 50 generations from the statistics). Only 3,000,000 active histories were used for those cases, SB-5 and Zebra-8H, because they require substantially more computer time per history than the other cases (350 generations). Nonetheless, the standard deviation for keff from those cases is comparable to those for other cases in the suite. This number of histories is sufficient to render the statistical uncertainty from the MCNP5 calculations essentially negligible relative to the benchmark uncertainty for most of the cases in the suite. The cases in the criticality validation suite can be summarized in Table 4.2.

Table 4.2 Description of MCNP Criticality Validation Suite

| Name | Spectrum | Handbook ID | Description |
| --- | --- | --- | --- |
| Jezebel-233 | Fast | U233-MET-FAST-001 | Bare sphere of 233U |
| Flattop-23 | Fast | U233-MET-FAST-006 | Sphere of 233U reflected by normal U |
| U233-MF-05 | Fast | U233-MET-FAST-005, case 2 | Sphere of 233U reflected by beryllium |
| Falstaff-1 | Intermediate | U233-SOL-INTER-001, case 1 | Sphere of uranyl fluoride solution enriched in 233U |
| SB-2½ | Thermal | U233-COMP-THERM-001, case 3 | Lattice of 233U fuel pins in water |
| ORNL-11 | Thermal | U233-SOL-THERM-008 | Large sphere of uranyl nitrate solution enriched in 233U |
| Godiva | Fast | HEU-MET-FAST-001 | Bare HEU sphere |
| Tinkertoy-2 | Fast | HEU-MET-FAST-026, case C-11 | 3 x 3 x 3 array of HEU cylinders in paraffin box |
| Flattop-25 | Fast | HEU-MET-FAST-028 | HEU sphere reflected by normal U |
| Godiver | Fast | HEU-MET-FAST-004 | HEU sphere reflected by water |
| Zeus-2 | Intermediate | HEU-MET-INTER-006, case 2 | HEU platters moderated by graphite and reflected by copper |
| UH3 | Intermediate | HEU-COMP-INTER-003, case 6 | UH3 cylinders reflected by depleted uranium |
| SB-5 | Thermal | U233-COMP-THERM-001, case 6 | Lattice of HEU fuel pins in water, with blanket of ThO2 pins |
| ORNL-10 | Thermal | HEU-SOL-THERM-032 | Large sphere of HEU nitrate solution |
| IEU-MF-03 | Fast | IEU-MET-FAST-003 | Bare sphere of IEU (36 wt.%) |
| BIG TEN | Fast | IEU-MET-FAST-007 | Cylinder of IEU (10 wt.%) reflected by normal uranium |
| IEU-MF-04 | Fast | IEU-MET-FAST-004 | Sphere of IEU (36 wt.%) reflected by graphite |
| Zebra-8H | Intermediate | MIX-MET-FAST-008, case 7 | IEU (37.5 wt.%) reflected by normal U and steel |
| IEU-CT-02 | Thermal | IEU-COMP-THERM-002, case 3 | Lattice of IEU (17 wt.%) fuel rods in water |
| STACY-36 | Thermal | LEU-SOL-THERM-007, case 36 | Cylinder of IEU (9.97 wt.%) uranyl nitrate solution |
| B&W XI-2 | Thermal | LEU-COMP-THERM-008, case 2 | Large lattice of LEU (2.46 wt.%) fuel pins in borated water |
| LEU-ST-02 | Thermal | LEU-SOL-THERM-002, case 2 | Sphere of LEU (4.9 wt.%) uranyl fluoride solution |
| Jezebel | Fast | PU-MET-FAST-001 | Bare sphere of plutonium |
| Jezebel-240 | Fast | PU-MET-FAST-002 | Bare sphere of plutonium (20.1 at.% 240Pu) |
| Pu Buttons | Fast | PU-MET-FAST-003, case 103 | 3 x 3 x 3 array of small cylinders of plutonium |
| Flattop-Pu | Fast | PU-MET-FAST-006 | Plutonium sphere reflected by normal U |
| THOR | Fast | PU-MET-FAST-008 | Plutonium sphere reflected by thorium |
| PU-MF-11 | Fast | PU-MET-FAST-011 | Plutonium sphere reflected by water |
| HISS/HPG | Intermediate | PU-COMP-INTER-001 | Infinite, homogeneous mixture of plutonium, hydrogen, and graphite |
| PNL-33 | Thermal | MIX-COMP-THERM-002, case 4 | Lattice of mixed-oxide fuel pins in borated water |
| PNL-2 | Thermal | PU-SOL-THERM-021, case 3 | Sphere of plutonium nitrate solution |

This suite can provide a general indication of the overall performance of a nuclear data library, and is not an absolute indicator of the accuracy or reliability of a given nuclear data library.

Table 4.3. Isotopes in these benchmarks models.

| Name | Name | Isotopes |
| --- | --- | --- |
| U233 | Jezebel-233 | 92235 92234 92233 92238 |
|  | Flattop-23 | 92233 92234 92235 92238 |
|  | U233-MF-05 | 92233 92234 92238 4009 8016 |
|  | Falstaff-1 | 92234 92233 92232 92238 92235 9019 8016 26057 26056 26054 24052 24050 26058 28058 24054 24053 28062 28061 28060 28064 4009 |
|  | SB-2½ | 8016 40090 40091 40092 40094 40096 92233 92234 92238 50112 50114 50115 50116 50117 50118 50119 50120 50122 50124 1001 26054 26056 26057 26058 5010 24050 24052 24053 24054 25055 28058 28060 28061 28062 28064 |
|  | ORNL-11 | 92233 92234 92235 92238 7014 8016 1001 90232 13027 14028 14029 14030 26054 26056 26057 26058 29063 29065 25055 |
| HEU | Godiva | 92235 92238 92234 |
|  | Tinkertoy-2 |  |
|  | Flattop-25 | 92234 92235 92238 |
|  | Godiver | 92234 92235 92236 92238 1001 8016 |
|  | Zeus-2 | 92234 92235 92236 92238 12024 12025 12026 13027 14028 14029 14030 22046 22047 22048 22049 22050 24050 24052 24053 24054 25055 26054 26056 26057 26058 29063 29065 6000 |
|  | UH3 |  |
|  | SB-5 | 8016 40090 40091 40092 40094 40096 92234 92235 92238 90232 64152 64154 64155 64156 64157 64158 64160 50112 50114 50115 50116 50117 50118 50119 50120 50122 50124 1001 26054 26056 26057 26058 5010 24050 24052 24053 24054 25055 28058 28060 28061 28062 28064 6000 |
|  | ORNL-10 | 92233 92234 92235 92236 92238 1001 7014 8016 13027 14028 14029 14030 25055 26054 26056 26057 26058 29063 29065 |
| LEU | B&W XI-2 | 5010 8016 92234 92235 92238 12024 12025 12026 13027 14028 14029 14030 22046 22047 22048 22049 22050 24050 24052 24053 24054 25055 26054 26056 26057 26058 29063 29065 1001 5011 |
|  | LEU-ST-02 | 92234 92235 92238 9019 1001 8016 13027 14028 14029 14030 29063 29065 25055 |

| IEU | IEU-MF-03 | 92234 92235 92238 26054 26056 26057 26058 6000 29063 29065 28058 28060 28061 28062 28064 74182 74183 74184 74186 |
| --- | --- | --- |
|  | BIG TEN | 92234 92235 92236 92238 14028 14029 14030 24050 24052 24053 24054 25055 26054 26056 26057 26058 28058 28060 28061 28062 28064 41093 |
|  | IEU-MF-04 | 92234 92235 92238 26054 26056 26057 26058 6000 74182 74183 74184 74186 |
|  | Zebra-8H | 92235 92238 6000 26054 26056 26057 26058 14028 14029 14030 1001 13027 8016 24050 24052 24053 24054 28058 28060 28061 28062 28064 42092 42094 42095 42096 42097 42098 42100 25055 29063 29065 22046 22047 22048 22049 22050 23000 |
|  | IEU-CT-02 | 92234 92235 92238 8016 26054 26056 26057 26058 24050 24052 24053 24054 28058 28060 28061 28062 28064 25055 14028 14029 14030 22046 22047 22048 22049 22050 6000 1001 64152 64154 64155 64156 64157 64158 64160 13027 |
|  | STACY-36 | 1001 7014 8016 92234 92235 92236 92238 6000 14028 14029 14030 25055 15031 16032 16033 16034 16036 28058 28060 28061 28062 28064 24050 24052 24053 24054 26054 26056 26057 26058 |
| PU | Jezebel | 94239 94240 94241 31000 |
|  | Jezebel-240 | 94239 94240 94241 94242 31000 |
|  | Pu Buttons | 94239 94240 94241 94242 13027 26054 26056 26057 26058 |
|  | Flattop-Pu | 94239 94240 94241 31000 92234 92235 92238 |
|  | THOR | 94239 94240 94241 31000 90232 |
|  | PU-MF-11 | 94239 94240 94241 94242 1001 8016 |
|  | HISS/HPG | 1001 5010 5011 6000 8016 20040 20042 20043 20044 20046 20048 94239 94240 94241 94242 |
|  | PNL-33 |  |
|  | PNL-2 | 94238 94239 94240 94241 94242 7014 1001 8016 26054 26056 26057 26058 24050 24052 24053 24054 28058 28060 28061 28062 28064 25055 |

Table 4.4. Results for the Criticality Validation Suite

|  |  | Description | Benchmark | ENDF/B-VII R. D. Mosteller | NRG JEFF3.0 | NRG JEFF3.1 | NEA JEFF3.1 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| PU | Fast | Jezebel | 1.00000 (200) | 0.99980 (30) | 1.00052 (40) | 1.00010 (19) | 1.00038 (26) |
|  |  | Jezebel-240 | 1.00000 (200) | 1.00030 (30) | - | 1.00428 (67) | 1.00337 (27) |
|  |  | Pu Buttons | 1.00000 (300) | 099840 (30) | - | - | 0.99698 (30) |
|  |  | Flattop-Pu | 1.00000 (300) | 1.00040 (30) | 0.99492 (44) | 1.00267 (43) | 1.00277 (31) |
|  |  | THOR | 1.00000 (60) | 1.00790 (30)* | 1.00937 (45) | 1.00305 (35) | 1.00271 (27) |
|  |  | Pu-MF-11 | 1.00000 (100) | 0.99920 (40) | - | - | 0.99722 (34) |
|  | Interm | HISS/HPG | 1.00000 (1100) | 1.01060 (20) | 1.00608 (57) | 1.00716 (44) | 1.00654 (42) |
|  | Thermal | PNL-33 | 1.00240 (210) | 1.00630 (30) |  |  |  |
|  |  | PNL-2 | 1.00000 (650) | 1.00290 (50) | - | - | 1.00504 (43) |
| U233 | Fast | Jezebel-233 | 1.00000 (100) | 0.99970 (30) | 1.01359 (38) | 1.00445 (107) | 1.00379 (24) |
|  |  | Flattop-23 | 1.00000 (140) | 0.99940 (30) | 1.00391 (53) | 1.00608 (44) | 1.00612 (30) |
|  |  | U233-MF-05_case2 | 1.00000 (300) | 0.99790 (30) | 1.00710 (49) | 1.00033 (48) | 1.00010 (30) |
|  | Interm | Falstaff_case1 | 1.00000 (830) | 0.99050 (50) | - | - | 0.98416 (48) |
|  | Therm | SB_2.5 | 1.00000 (240) | 0.99880 (40) | 0.99848 (112) | 0.99761 (112) | 0.99700 (44) |
|  |  | ORNL-11 | 1.00060 (290) | 1.00410 (20) | - | - | 0.99723 (17) |
| HEU | Fast | Godiva | 1.00000 (100) | 0.99940 (30) | 0.99596 (40) | 0.99644 (19) | 0.99696 (27) |
|  |  | Tinkertoy-2 | 1.00000 (380) | 1.00040 (30) |  |  |  |
|  |  | Flattop-25 | 1.00000 (300) | 1.00290 (30) | 0.99379 (43) | 1.00275(51) | 1.00220 (28) |
|  |  | Godiver | 0.99850 (110) | 0.99780 (40) | - | - | 0.99444 (32) |
|  | Intermediate | Zeus-2 | 1.00010 (80) | 0.99580 (40) | 0.99394 (90) | 0.99540 (84) | 0.99490 (35) |
|  |  | UH3 | 1.00000 (470) | 0.99520 (40) |  |  |  |
|  | Thermal | SB-5 | 1.00150 (280) | 0.99570 (50) | - | 0.99731 (102) | 0.99797 (50) |
|  |  | ORNL-10 | 1.00150 (260) | 0.99890 (20) | - | 0.99855 (37) | 0.99874 (17) |
| IEU | Fast | IEU-MF-03 | 1.00000 (170) | 1.00270 (30) | - | - | 0.99897 (27) |
|  |  | BIG-TEN | 0.99480 (130) | 0.99520 (20) | 1.00058 (28) | 0.99798 (28) | 0.99774 (23) |
|  |  | IEU-MF-04 | 1.00000 (300) | 1.00720 (30) | - | - | 1.00379 (28) |
|  | Intermediate | Zebra-8H | 1.03000 (250) | 1.01980 (20) | - | - | 1.01579 (23) |
|  | Thermal | IEU-CT-02_c3 | 1.00170 (440) | 1.00080 (30) | 0.99987 (80) | 0.99941 (82) | 1.00081 (33) |
|  |  | STACY-36 | 0.99880 (130) | 0.99940 (30) | 0.99920 (56) | 1.00109 (67) | 0.99860 (20) |
| LEU | Thermal | BaW XI_2 | 1.00070 (120) | 1.00000 (30) | - | - | 0.99984 (30) |
|  |  | LEU-ST-02_c2 | 1.00240 (370) | 0.99610 (30) | - | - | 0.99630 (28) |

*Cases with differences more than 2* are marked in red.

In conclusion:

- For PU:

  - Deficiencies in fast cases

- For U233:

  - Deficiencies in fast cases

- For HEU:

  - Deficiencies in fast and intermediate cases

  - Improvement in thermal case SB-5

- For IEU:

  - Deficiencies in fast and intermediate cases

  - Improvements in IEU-MF-03 (bare) and IEU-MF-04 (light reflector)

- For LEU:

  - Good approximation (need for ad hoc adjustment to 238U resonance integral may be eliminated)

### Additional Validation

Some interesting Benchmark have been evaluated  in [LA-UR-05-8430].

This Validation Suite is included in Reference [ICSBEP].

Most of them are not in electronic format, so a tedious hand-work has been performed to process these files.

Table 4.5. Additional criticality validation tests from ICSBEP.

|  |  | Case | Benchmark | ENDF/B-VII R. D. Mosteller | NEA JEFF3.1 |
| --- | --- | --- | --- | --- | --- |
| PU | Thermal | PU-SOL-THERM-009 (48-inch sphere of plutonium nitrate solution) | 1.00030 (330) | 1.01910 (20) | 1.01515 (49) |
|  |  | Same sphere as for ORNL-10 (HEU) and ORNL-11 (U233) Benchmarks Very thermal spectra with vey little leakage Cross sections for Pu239 should be re-examined in the deep thermal range |
| HEU | Fast | HEU-MET-FAST-73 (Unmoderated ZEUS benchmark) | 1.00120 (150) | 1.00800 (30) | 1.00849 (26) |
|  |  | Benchmark contains no moderator and therefore has a fast spectrum Fast cross sections for Cu should be reviewed |
| HEU | Thermal | HEU-SOL-THERM-004_case1 (Heavy water solutions, reflected spheres) | 1.00000 (330) | 0.98390 (40) | 0.98438 (38) |
|  |  | Improvement for cases with deuterium d |
| SPEC | Thermal | SPEC-MET-FAST-08 (Neptunium sphere reflected by HEU) | 1.00190 (360) | 0.99240 (30) | 0.99177 (24) |
|  |  | Fast cross sections for Np-237 should be reviewed |

## Radiation-Shielding validation Suite

The present benchmark calculations use specifications given in the SINBAD Database [SINBAD]. Other references have been used to compare these calculations [ALEPH-DLG , JEFDOC-1106].

### EURAC-Fe

Ispra Iron Benchmark Experiment (EURACOS). Study of the neutron deep penetration in homogeneous materials commonly used in the construction of advanced reactors: Fe (and Na). Flux and spectra were measured up to 130 cm in Fe.

Table 4.6. Results for EURAC-Fe using different data libraries

| Distance (cm) | measured | cell | Endf60 | NRG JEFF-3.1 | Endf-602 + Fe56 (JEFF-3.1) | NEA JEFF-3.1 |
| --- | --- | --- | --- | --- | --- | --- |
| 54 | 2.872e+0 | 47 | 2.746E+00 | 2.742E+00 | 3.738E+00 | 3.997E+00 |
| 62 | 6.398e-1 | 48 | 6.717E-01 | 6.652E-01 | 9.503E-01 | 1.013E+00 |
| 70 | 1.338e-1 | 49 | 1.615E-01 | 1.595E-01 | 2.390E-01 | 2.537E-01 |
| 78 | 3.045e-2 | 50 | 3.880E-02 | 3.769E-02 | 5.991E-02 | 6.331E-02 |
| 86 | 7.025e-3 | 51 | 9.274E-03 | 9.115E-03 | 1.501E-02 | 1.577E-02 |
| 94 | 2.372e-3 | 52 | 2.227E-03 | 2.161E-03 | 3.780E-03 | 3.936E-03 |

Significant differences are obtained mainly due to Fe56.

### KANT

KANT Spherical Shell Transmission Experiment on Beryllium. The purpose at the time of the experiment was mainly to clarify the discrepancies found by other researchers in the effective neutron multiplication of bulk beryllium assemblies with central 14 MeV neutron sources.

Recorded neutron leakage spectra from 5, 10 and 17 cm thick spherical beryllium shells from the source energy down to less than 10 eV is evaluated.

The KANT input included in SINBAD Database has a problem with the geomtry.

It stops before end with the message:

“run terminated because  10 particles got lost”

Finally, an updated input has been included in SINBAD Database by A.Serikov and D. Leichtle/U.Fischer in March 2006.

Figure 4.1. Normalized leakage neutron fluence from 17 cm Be shell. KANT Experiment.

### VENUS

The VENUS Critical Facility is a zero power reactor located at CEN/SCK, Mol (Belgium).

There is a problem with the geometry: MCNP4C2 does not run this case.

### NIST

A Cf source was placed at the centre of the experiment, and fission foils were palced at two, diametrically oposed positions. Between the source and the fission foils were several combinations of shielding materials.

### NoCd+NoWater+2,0"

Table 4.7. C/E values for the fission rates in the NIST benchmark

| Bare= NoCd+NoWater+2,0" |
| --- |
|  | Exper. |  | Tally2 |  | MCNP | MCNP*4*pi*r**2 |  | LA-13675 |
|  | (b) | (%) | <xs*flux> | error | Fission rates | Fission rates | MCNP-JEFF-3.1 C/E | MCNP-ENDFB-V C/E |
| U235 | 1,279 | 1,6 | 1,73E-03 | 0,001 | 1,73E-03 | 1,27E+00 | 0,989 | 1,006 | 0,017 |
| Pu239 | 1,924 | 1,5 | 2,55E-03 | 0,001 | 2,55E-03 | 1,86E+00 | 0,966 | 0,965 | 0,016 |
| U238 | 0,334 | 1,7 | 4,33E-04 | 0,001 | 4,33E-04 | 3,16E-01 | 0,945 | 0,940 | 0,018 |
| Np237 | 1,42 | 1,8 | 1,90E-03 | 0,001 | 1,90E-03 | 1,38E+00 | 0,975 | 0,969 | 0,019 |

### Cd+Water+2,5"

Table 4.8. C/E values for the fission rates in the NIST benchmark

| Cd+Water+2,5" |
| --- |
|  | Exper. |  | Tally2 |  | MCNP | MCNP*4*pi*r**2 |  | LA-13675 |
|  | (b) | (%) | <xs*flux> | error | Fission rates | Fission rates | MCNP-JEFF-3.1 C/E | MCNP-ENDFB-VI C/E |
| U235 | 5,86 | 1,7 | 5,14E-03 | 0,005 | 5,14E-03 | 5,86E+00 | 1,000 | 1,048 | 0,035 |
| Pu239 | 7,74 | 1,9 | 6,58E-03 | 0,006 | 6,58E-03 | 7,50E+00 | 0,969 | 0,977 | 0,042 |
| U238 | 0,171 | 1,9 | 1,42E-04 | 0,004 | 1,42E-04 | 1,62E-01 | 0,946 | 0,941 | 0,03 |
| Np237 | 0,748 | 1,9 | 6,34E-04 | 0,003 | 6,34E-04 | 7,22E-01 | 0,966 | 0,945 | 0,026 |

### IPPE-FE

IPPE neutron transmission benchmark experiment with 14 MeV neutrons through iron shells. Neutron leakage spectra between 50 keV and 15 MeV from five iron shells were measured by the time-of-flight technique using a 14 MeV neutron generator. The spheres had radius from 4.5 to 30.0 cm and wall thicknesses from 2.5 to 28.0 cm.

Figure 4.2. Neutron leakage spectra for iron shell No. 1: Experimental values versus MCNP4c2 calculation.

### FNS: Oxygen

The  neutron spectrum emerging from slabs of material of varying thickness, was measured at five different angles. The slabs were placed at 20 cm distance from a 14 MeV D-T neutron source.

The input included in SINBAD Database does not run with MCNP4c.

- A problem in soubroutine calcps.f, in line:

erg=eg0*(t1*(cs+sqrt(cs**2-t3)))**2

where cs**2<t3

This input runs with MCNP4c2.

The normalization factor used is: Flux experimental=Fluxcalculated*L2/As

Figure 4.3. Neutron spectrum for the FNS, O, 20 cm, at 0 ºangle.

### Oktavian: Al

In the Oktavian benchmark, the leakage current spectrum from the outer surface of a spherical pile of material is measured. At the centre of a pile a 14 MeV D-T neutron source was located.

Figure 4.4. Result for the neutron leakage spectrum for the Oktavian Al benchmark

### LLNL Pulsed Spheres: Iron, 4.8 MFP

These pulsed sphere experiments was performed by Lawrence Livermore National Laboratory (LLNL). Time-of-flight meausurements were performed for neutrons passing trough spherical shells of varying thickness, containing different materials. The source was a 14 MeV D-T neutron source. [LA-12885]

These experiments are more sensitive to cross section data and even angular distributions when compared to integral benchmarks.

Figure 4.5. Neutron spectrum for the LLNL Pulsed sphere, iron, 4.8 mfp.

# References

[ACELST] Trkov, A., ACELST code, December 2002.

[ADS-Lib/V1.0] D. López Aldama and A. Trkov, A test library for Accelerator Driven Systems, ADS-Lib/V1.0 , IAEA, 2005.

[ANRCP-1999-28] M.S. Abdelrahman, N. Abdurrahman, Cross Section Libraries for Studies of Plutonium Disposition in Light Water Reactors. ANRCP-1999-28, October 1999.

[ALEPH-DLG] W. Haeck, B. Verboomen, ALEPH-DLG 1.1.0 Creating Cross Section Libraries for MCNP(X). SCK, CEN-BLG-1002 Rev. 0. February, 2006.

[ENDF2ACE] J. Perrot, O. Meplan, ENDF2ACE User Guide,

http://lpsc.in2p3.fr/gpr/MURE/html/ENDF2ACE_User_Guide/

[ENDF60] S. C. FRANKLE, Experience with ENDF60 and QA of a Continuous-Energy Library, XTM:SCF-96-363, Los Alamos National Laboratory, USA (1996)

[ICSBEP] J. Blair Briggs (ed.), International Handbook of Evaluated Criticality Safety Benchmark Experiments, NEA/NSC/DOC(95)03/I, Nuclear Energy Agency, Paris (September 2005 Edition)

[JEFDOC-1106] S.C. van der Marck, Shielding benchmark calculations with MCNP-4C3 using JEFF-3.1 data, NRG-Petten, October 2005, JEFDOC-1106.

[JEFDOC-1107] S.C. van der Marck, Criticality safety benchmark calculations with MCNP-4C3 using JEFF-3.1 data, NRG-Petten, October 2005, JEFDOC-1107.

[JEFF-3.1] NEA/OECD; “The JEFF-3.1 project: Complete content of the JEFF-3.1 evaluated nuclear data library”, June 2, 2005, NEA#06071 (on CDROM)

[LA-UR-98-5718] Robert C. Little, Robert E. MacFarlane, ENDF/B-VI Neutron Library for MCNP with Probabity Tables, LANL, LA-UR-98-5718, Dec. 1998

[LA-UR-05-8430] Russell D. Mosteller, Comparison of ENDF/B-VI and Initial ENDF/B-VII Results for the MCNP Criticality Validation Suite, LA-UR-05-8430, 2005.

[LA-UR-98-5718] R. C. LITTLE, R. E. MacFARLANE, .ENDF/B-VI Neutron Library for MCNP with Probability Tables., LA-UR-98-5718, Los Alamos National Laboratory, USA (1998)

[LA-UR-02-1235] M. C. WHITE, J. M. CAMPBELL, S. C. FRANKLE, R. C. LITTLE, Processing of Nuclear Data for Applications., LA-UR-02-1235, Los Alamos National Laboratory, USA (2002)

[LA-UR-03-0954] J. M. CAMPBELL, S. C. FRANKLE, R. C. LITTLE, .ENDF66: A Continuous-Energy Neutron Data Library Based on ENDF/B-VI Release 6., LA-UR-03-0954, Los Alamos National Laboratory, USA (2003)

[LA-12885] J. D. Court, R.C. Brockhoff, and J.S. Hendricks Lawrence Livermore Pulsed Sphere Benchmark Analysis of MCNP ENDF/B-VI, LA-12885 (1994)

[MCNP4c] Briesmeister, J. F., “MCNP – A General Monte Carlo N-Particle Transport Code, Version 4C”, Los Alamos National Laboratory, LA-13709-M, 2000

[NDC(NDS)-0470] M. Mattes and J. Keinert, Thermal Nutron Scattering Data for the Moderator materials H2O, D2O and ZrHx in ENDF-6 Format and as ACE library for MCNP(X) Codes, INDC(NDS)-0470, April 2005

[NJOY-99] MacFarlane, R.E., Muir, D.M., “NJOY-99.0: Code System for Producing Pointwise and Multigroup Neutron and Photon Cross Sections from ENDF/B data”, Los Alamos National Laboratory, PSR-480, 2000.

[NJOY99_up90] R. E. MacFARLANE, .up90 - NJOY version 99.90., Los Alamos National Laboratory, USA (2003)

[NJOY90_up112] R. E. MacFARLANE, .up112 - NJOY version 99.112., Los Alamos National Laboratory, USA (2005)

[PREPRO2004] Cullen, D.E., “PREPRO 2004: 2004 ENDF/B Pre-processing codes”, IAEA-NDS-39, Rev. 12, November 22, 2004.

[SINBAD] Sinbad data base, NEA (2005).

[UpdXSDIR] Trkov, A., UpdXSDIR code, December 2002.

[YUCCA] F.A. Alpan, M.E. Dunn, Yummy: The Yucca Mountain MCNP-Library, ORNL/TM-2204/124, June 2004.

# APENDIX A

Inputs for Scattering Thermal Libraries

## A.1 Be at 1200K

moder / Extract thermal Scattering Law

1 -61

' 4-Be     from JEFF3.1'/

60 26

0/

moder / Extract/convert neutron evaluated data

1 -21

'4-Be from JEFF3.1'/

20 425

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 4-Be'/

425 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 4-Be from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

425 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1200.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 425 12 1 1  2 1 221 1/

1200.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

26 425 16 1 4  2 1 231 1/

1200.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'4-Be    1200.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

425 1200.0 'bena08' /

4009    0    0 /

231 64 232  0  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.2 Be in BeO at 1200K

moder / Extract thermal Scattering Law

1 -61

' 4-Be     from JEFF3.1'/

60 26

0/

moder / Extract/convert neutron evaluated data

1 -21

'4-Be from JEFF3.1'/

20 425

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 4-Be'/

425 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 4-Be from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

425 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1200.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 425 12 1 1  3 1 221 1/

1200.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

26 425 16 1 4  3 2 233 1/

1200.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'4-Be    1200.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

425 1200.0 'beo08 ' /

4009 8016    0 /

233 64 234  0  2 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.3 D in D2O at 643.9K

moder / Extract thermal Scattering Law

1 -61

' D-D2O    from JEFF3.1'/

60 11

0/

moder / Extract/convert neutron evaluated data

1 -21

'1-H-2 from JEFF3.1'/

20 128

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 1-H-2'/

128 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 1-H-2 from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

128 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

643.9

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 128 12 1 1  0 1 221 1/

643.9

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

11 128 16 1 4  0 2 228 1/

643.9

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'D-D2O   643.9 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

128 643.9 'hwtr08' /

1002    0    0 /

228 64   0  0  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.4 H in H2O at 1000K

moder / Extract thermal Scattering Law

1 -61

' H-H2O    from JEFF3.1'/

60 1

0/

moder / Extract/convert neutron evaluated data

1 -21

'1-H-1 from JEFF3.1'/

20 125

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 1-H-1'/

125 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 1-H-1 from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

125 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1000.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 125 12 1 1  0 1 221 1/

1000.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

1 125 16 1 4  0 2 222 1/

1000.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-H2O   1000.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 1000.0 'lwtr11' /

1001    0    0 /

222 64   0  0  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.5 H in HZr at 1200K

moder / Extract thermal Scattering Law

1 -61

' H-ZrH    from JEFF3.1'/

60 7

0/

moder / Extract/convert neutron evaluated data

1 -21

'1-H-1 from JEFF3.1'/

20 125

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 1-H-1'/

125 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 1-H-1 from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

125 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1200.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 125 12 1 1 12 1 221 1/

1200.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

7 125 16 1 4 12 2 225 1/

1200.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-ZrH   1200.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 1200.0 'hzrh08' /

1001    0    0 /

225 64 226  1  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.6 H in CH2 at 350K

moder / Extract thermal Scattering Law

1 -61

' H-CH2    from JEFF3.1'/

60 37

0/

moder / Extract/convert neutron evaluated data

1 -21

'1-H-1 from JEFF3.1'/

20 125

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 1-H-1'/

125 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 1-H-1 from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

125 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

350.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 125 12 1 1 11 1 221 1/

350.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

37 125 16 1 4 11 2 223 1/

350.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-CH2   350.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 350.0 'poly02' /

1001    0    0 /

223 64 224  1  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

## A.7 Graphite  at 3000K

moder / Extract thermal Scattering Law

1 -61

' Graphi   from JEFF3.1'/

60 31

0/

moder / Extract/convert neutron evaluated data

1 -21

'6-C from JEFF3.1'/

20 600

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 6-C'/

600 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 6-C from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

600 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

3000.0

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 600 12 1 1  1 1 221 1/

3000.0

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

31 600 16 1 4  1 1 229 1/

3000.0

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'Graphi  3000.0 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

600 3000.0 'grph11' /

6000    0    0 /

229 64 230  0  1 4.0 0/

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

# APENDIX B

Inputs for NJOY processing

## B.1 Ag109 at 1200K (without PURR module)

moder / Extract/convert neutron evaluated data

1 -21

'47-Ag-109 from JEFF3.1'/

20 4731

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 47-Ag-109'/

4731 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 47-Ag-109 from JEFF3.1'/

'Processed by NJOY-99.90 at NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

4731 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1000.

0/

heatr / Add heating kerma and damage energy

-21 -23 -24/

4731 7 0 0 0 2/

302 303 304 318 402 443 444/

gaspr / Add gas production

-21 -24 -25

thermr / Add thermal scattering data

0 -25 -26

0 4731 12 1 1 0 1 221 1/

1000.

0.001 4.0

1000.

1.E+10

0/

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .38/

'47-Ag-109 from JEFF3.1(JEFF3.1) NJOY 99.90 NEA Oct2005'/

4731 1000.

1 1/

/

acer / Check ACE files

0 27 0 29 30

7 1 1 -1/

/

stop

## B.2 U235 at 300K (with PURR module)

moder / Extract/convert neutron evaluated data

1 -21

'92-U-235 from JEFF3.1'/

20 9228

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 92-U-235'/

9228 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 92-U-235 from JEFF3.1'/

'Processed by NJOY-99.90 at NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

9228 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

1000.

0/

heatr / Add heating kerma and damage energy

-21 -23 -24/

9228 7 0 0 0 2/

302 303 304 318 402 443 444/

gaspr / Add gas production

-21 -24 -25

thermr / Add thermal scattering data

0 -25 -41

0 9228 12 1 1 0 1 221 1/

1000.

0.001 4.0

purr / Process Unresolved Resonance Range if any

-21 -41 -26

9228 1 1 20 100/ matd ntemp nsigz nbin nladr

1000.

1.E+10

0/

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .38/

'92-U-235 from JEFF3.1(JEFF3.1) NJOY 99.90 NEA Oct2005'/

9228 1000.

1 1/

/

acer / Check ACE files

0 27 0 29 30

7 1 1 -1/

/

stop

# APENDIX C

NJOY patchs ( the rest of the patch will be included in electronic format)

## C.1 upn90_noup63_noup56

REM -----

REM upn90_noup63_noup56 : (included in upn_Hogenbirk)

REM                  - Include upn90 except for:

REM                  - up63 to treat delayed neutrons (updated in upn_Hogenbirk)

REM                  - up64, up72 and up75 do not include updates for up63

REM                  - up56: converting law7 into law1

REM                  - up64 does not include update for up56

REM

*cpl all

*set sw

*ident up1

*/ leapr -- 04apr00

*/ this fixes errors that destroy the calculation of s(alpha,beta)

*/ for cold para-hydrogen and for both cold deuteriums.  the first

*/ was introduced in 97.53 while making the constants symbolic,

*/ and the second was introduced in the cleanup process for njoy99.

*d leapr.1902

if (law.gt.3) de=ded

*d leapr.2121

sum2=(sjbes(jp,y)*cn(j,jp,jp))**2

*ident up2

*/ groupr -- 04apr00

*/ there is an error in the indexing for the xmas 172-group structure

*/ that throws all the group bounds off by one.  this structure is

*/ used in europe for thermal reactor calculations.

*d groupr.1835

eg(ig)=eg18(174-ig)

*/ fix a problem introduced with the activation patch of 97.102.  the

*/ nk parameter is only used when doing mf values for activation

*/ products, and it is not appropriate for fission nubar values.

*d groupr.3824

nk=0

if (mf.gt.99) nk=nint(a(iyld+4))

*i groupr.3853

if (nk.eq.0) go to 180

*/ don't strip off the upscatter groups for the neutron spectra

*/ coming from delayed neutron emission (mt=455).

*d groupr.8913

if (mfd.ne.15.and.mtd.ne.455) then

*/ add a missing save statement and fix an unset variable in anased.

*/ these problems affect delayed neutron spectra.

*d groupr.8983

save new,theta,xc,rc,bot,ca,loct

*i groupr.9050

np=nint(a(loct+6))

*ident up3

*/ acer -- 04apr00

*/ the acer consistency checks include an option to readjust

*/ eprime values that are greater than e, when appropriate.

*/ there are some problems with the logic, especially for

*/ cases that use histogram interpolation for the distribution.

*i acer.18017

ishift=j-nn-1

*d acer.18019

xss(j+loci)=sigfig(epmax,7,ishift)

*i acer.18022

xss(j-1+nn+loci)=p

xss(j+nn+loci)=p

*i acer.18026

xss(j+nn+loci)=p

*d acer.18028

*i acer.18131

xss(j-1+nn+loci)=p

xss(j+nn+loci)=p

*i acer.18135

xss(j+nn+loci)=p

*d acer.18137

*/ when using the old format (mcnp4b and earlier), some angle-energy

*/ distributions from file 6 are converted into the law 67 format,

*/ because these earlier versions of mcnp couldn't use all the

*/ file 6 representations.  when converting from the cm to the lab,

*/ the methods used in subroutine fix6 are a little crude.  they get

*/ confused when cm energies are so small that lab cosines of -1

*/ are not reached.  this patch tries to fix that in a rough way,

*/ but evaluations that use the cm frame in file 6 will work best

*/ if most of the cm energies are greater than e/(awr+1)**2 for

*/ each incident energy e.  for mcnp4c and later, the code can

*/ sample directly from tabulated cm representations, and the

*/ approximations of the fix6 routine are avoided.  this patch

*/ is needed for one evaluation from JEFF-3.

*d acer.3238

*i acer.3250

data namax/1000/

*d acer.3353

if (lct.ne.1) then

*d acer.3372

if (ep.gt.zero) then

csn=clb*sqrt(elb/ep)-sqrt(ein/ep)/aw1

endif

*i acer.3398,3420

if (j.le.l2+8.or.elb.gt.a(j-2)) then

a(j)=elb

a(j+1)=fmu*drv

j=j+2

endif

if (j.ge.namax-1) call error('fix6',

&              'storage in a exceeded',' ')

*i acer.3421

nnep=(j-(l2+8))/2

if (nnep.eq.1) then

a(l2+10)=2*a(l2+8)

a(l2+11)=0

nnep=2

endif

a(l2+5)=nnep

a(l2+6)=nnep

j2=l2

call tab1io(0,nout,ndebug,a(j2),nb,nw)

do while (nb.ne.0)

j2=j2+nw

call moreio(0,nout,ndebug,a(j2),nb,nw)

enddo

*/ increase the available storage to handle the very large

*/ mf6/mt16 tabulation in JEFF-3 Be-9.

*d acer.226

common/astore/a(80000)

*d acer.235

data namax/80000/, nidmax/27/

*d acer.460

common/astore/a(80000)

*d acer.2130

data nwmaxn/65000/

*d acer.4672

common/astore/a(80000)

*d acer.5604

common/astore/a(80000)

*d acer.5765

common/astore/a(80000)

*d acer.5954

common/astore/a(80000)

*d acer.6326

common/astore/a(80000)

*d acer.7385

common/astore/a(80000)

*d acer.8058

common/astore/a(80000)

*d acer.8068

data namax/40000/

*d acer.9762

common/astore/a(80000)

*d acer.10677

common/astore/a(80000)

*d acer.13068

common/astore/a(80000)

*d acer.13464

common/astore/a(80000)

*d acer.14300

common/astore/a(80000)

*d acer.14665

common/astore/a(80000)

*d acer.15215

common/astore/a(80000)

*d acer.21814

common/astore/a(80000)

*/ increase the space available for discontinuities in convr

*/ to allow for JENDL-3.2 si-nat

*d acer.254

nned=50

*ident up4

*/ reconr -- 05apr00

*/ be sure to count subsections of file 12 before allocating

*/ storage for the elements of the new directory.  otherwise,

*/ some materials with many sections of file 12 will overflow.

*/ this is a longstanding problem that we never noticed before.

*i reconr.419

nxn=nxn+1

*ident up5

*/ purr -- 7may00

*/ fix a problem introduced while installing the heating part

*/ of the probability tables.  it shows up when doing elements

*/ that have unresolved data.  also, increase the number of

*/ resonance sections allowed to handle the very large cd-nat

*/ evaluation from JENDL.

*d purr.1076

e=abs(eunr(ie))

*d purr.1106,1108

common/sigcon/e,t,cth(50),csz(50),cc2p(50),cs2p(50),

&  cgn(50),cgg(50),cgf(50),cgx(50),cgt(50),dbar(50),

&  spot,dbarin,sigi(4),ndfn(50),ndff(50),ndfx(50),nseq0

*d purr.1139

*d purr.1187,1189

*d purr.1247

if (nseq0.gt.50) call error('unresx',

*d purr.1501,1503

common/sigcon/e,t,cth(50),csz(50),cc2p(50),cs2p(50),

&  cgn(50),cgg(50),cgf(50),cgx(50),cgt(50),dbar(50),

&  spot,dbarin,sigi(4),ndfn(50),ndff(50),ndfx(50),nseqz

*d purr.1621,1623

common/sigcon/e,t,cth(50),csz(50),cc2p(50),cs2p(50),

&  cgn(50),cgg(50),cgf(50),cgx(50),cgt(50),dbar(50),

&  spot,dbarin,sigi(4),ndfn(50),ndff(50),ndfx(50),nseqz

*d purr.1739,1741

common/sigcon/e,t,cth(50),csz(50),cc2p(50),cs2p(50),

&  cgn(50),cgg(50),cgf(50),cgx(50),cgt(50),dbar(50),

&  spot,dbarin,sigi(4),ndfn(50),ndff(50),ndfx(50),nseq0

*ident up6

*/ acer -- 30may00

*/ fix a typo in up3 (reported by bunde, anl)

*d up3.93

data namax/80000/

*/ acer -- 30may00

*/   fix problems with converting cm distributions to law=7

*/   and problems reading law=7 into the ace file.  these problems

*/   show up when running newfor=0 with njoy2000, especially on

*/   some materials from jef-2.2.

*d acer.3342

*d acer.3347,3348

*d acer.3364

c                       if(imu.lt.nmu.and.amu(imu+1).le.cmn) drv=0

*i acer.3377

c                    include jacobian for cm-to-lab transformation

if (ep.ne.zero) drv=drv*sqrt(elb/ep)

*d up3.46,up3.50

if (j.le.l2+8) then

a(j)=elb

a(j+1)=fmu*drv

j=j+2

else if (elb.gt.a(j-2)) then

a(j)=elb

a(j+1)=fmu*drv

j=j+2

endif

*d acer.3399,3420

if (iep.eq.nep) idone=1

*d acer.6330

external listio,terpa,terp1,bachaa,mess,fndar1,fndar2,skip6a

*d acer.6380

call skip6a(nin,0,0,a(jscr),law)

*d acer.6412

call skip6a(nin,0,0,a(jscr),law)

*d acer.6497

call skip6a(nin,0,0,a(jscr),law)

*i acer.6935

c

subroutine skip6a(nin,nout,nscr,a,law)

c     ******************************************************************

c     special version of skip6 for special version of File 6 used

c     in acer.  law=7 has a tab1 containing the angular distribution

c     instead of the normal tab2 for each incident energy.

c     skip the next subsection in the current section (mt).

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

common/cont/c1h,c2h,l1h,l2h,n1h,n2h,math,mfh,mth,nsh,nsp,nsc

dimension a(*)

c

if (law.eq.6) then

call contio(nin,nout,nscr,a(1),nb,nw)

else if (law.eq.1.or.law.eq.2.or.law.eq.5) then

call tab2io(nin,nout,nscr,a(1),nb,nw)

ne=n2h

do ie=1,ne

call listio(nin,nout,nscr,a(1),nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a(1),nb,nw)

enddo

enddo

else if (law.eq.7) then

call tab2io(nin,nout,nscr,a(1),nb,nw)

ne=n2h

do ie=1,ne

call tab1io(nin,nout,nscr,a(1),nb,nw)

nmu=n2h

do imu=1,nmu

call tab1io(nin,nout,nscr,a(1),nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a(1),nb,nw)

enddo

enddo

enddo

endif

return

end

*ident up7

*/ viewr -- 30may00

*/ increase the allowed size of 3d plots.

*/ pushed by pb-nat from jef-2.2.

*d viewr.680

if (l+5000.ge.maxaa) then

*d viewr.1295

dimension x(2000),y(2000),z(2000)

*d viewr.1304

kmax=1999

*ident up8

*/ acer -- 3jun00

*/ subroutine ptleg2 does not need the dynamic array xat.

*/ this problem was first noted by Waclaw Gudowski for ENDF/B-VI

*/ si-nat.  it shows up as "id xat not defined".

*d acer.5628

*d acer.5632

call ptleg2(a(iscr))

*d acer.5646

call ptleg2(a(iscr))

*d acer.6838,6839

call ptleg2(a(jscr))

*d acer.6937

subroutine ptleg2(a)

*d acer.6950

*d acer.8470,8471

call ptleg2(a(lld))

*d acer.8720

*d acer.8731

call ptleg2(a(lld))

*d acer.16034

*d acer.16037

call ptleg2(a(lld))

*ident up9

*/ acer -- 07jun00

*/  add the capability for processing anisotropic charged particle

*/  emission using tabulated legendre coefficients into the

*/  mcnp4c law61 format.  this is needed for jeff-3 cr-52.

*/  allow for multiple interpolation ranges in file 6.  this

*/  also occurs for jeff-3 cr-52.  currently, the neutron

*/  energy-angle distribution only allows for combinations of

*/  histogram and linear linear interpolation, but the

*/  charged-particle sections allow for general combinations of

*/  all allowed interpolation laws.

*d acer.6391

jnt=nint(a(jscr+5+2*m))

*i acer.6456

if (idis.eq.1.and.xx.lt..9999*xn) xn=sigfig(xn,7,-1)

*d acer.8278,8285

next=next+2

nrint=nint(a(iscr+4))

if (nrint.eq.1.and.nint(a(iscr+7)).eq.2) then

xss(next)=0

else

xss(next)=nrint

do i=1,nrint

xss(next+i)=nint(a(iscr+4+2*i))

xss(next+nrint+i)=nint(a(iscr+5+2*i))

enddo

next=next+2*nrint

endif

next=next+1

ne=nint(a(iscr+5))

xss(next)=ne

do i=1,ne

xss(next+i)=

&                       sigfig(a(iscr+4+2*nrint+2*i)/emev,7,0)

xss(next+i+ne)=

&                       sigfig(a(iscr+5+2*nrint+2*i),7,0)

enddo

next=next+1+2*ne

*d acer.9031,9032

*i acer.9033

lang=nint(a(ll+2))

lawnow=0

if (law.eq.1.and.lang.eq.1) lawnow=61

if (law.eq.1.and.lang.eq.2) lawnow=44

if (law.eq.2) lawnow=33

if (lawnow.eq.0) call error('acelcp',

&                    'unsupported law and lang',' ')

xss(last+1)=lawnow

*i acer.9090

nexcd=next+4*ng+2

*d acer.9121

c                                kalbach distribution

if (lang.eq.2) then

*i acer.9126

c                                legendre distribution

else if (lang.eq.1) then

ep=xss(next+1+ig)

a(ll)=0

a(ll+1)=ep

a(ll+2)=0

a(ll+3)=0

a(ll+4)=na

a(ll+5)=0

do ia=1,na

lll=lld+7+ncyc*(ig-1)

a(ll+5+ia)=0

if (a(lll).ne.zero) then

a(ll+5+ia)=a(lll+ia)/a(lll)

endif

enddo

call ptleg2(a(ll))

xss(next+1+3*ng+ig)=nexcd-dlwh+1

intmu=2

xss(nexcd)=intmu

nmu=nint(a(ll+5))

xss(nexcd+1)=nmu

do imu=1,nmu

xss(nexcd+1+imu)=sigfig(

&                                   a(ll+6+2*imu),7,0)

xss(nexcd+1+nmu+imu)=sigfig(

&                                   a(ll+7+2*imu),7,0)

if (imu.eq.1) then

xss(nexcd+1+2*nmu+imu)=0

else if (imu.eq.nmu) then

xss(nexcd+1+2*nmu+imu)=1

else

del=a(ll+6+2*imu)

&                                      -a(ll+4+2*imu)

av=(a(ll+7+2*imu)

&                                      +a(ll+5+2*imu))/2

xss(nexcd+1+2*nmu+imu)

&                                      =xss(nexcd+1+2*nmu+imu-1)

&                                      +del*av

xss(nexcd+1+2*nmu+imu)=sigfig

&                                      (xss(nexcd+1+2*nmu+imu),7,0)

endif

enddo

nexcd=nexcd+2+3*nmu

*d acer.9160

if (lang.eq.1) then

next=nexcd

else

next=next+2+(2*na+3)*ng

endif

*d acer.11158,11163

l2=sigh+l1+1

nrint=nint(xss(l2))

write(nsyso,'(4x,''nr ='',i4)') nrint

if (nrint.ne.0) then

write(nsyso,'(4x,''nbt(i=1,nr) = '',20i5)')

&           (nint(xss(l2+ii)),ii=1,nrint)

l2=l2+nrint

write(nsyso,'(4x,''int(i=1,nr) = '',20i5)')

&           (nint(xss(l2+ii)),ii=1,nrint)

l2=l2+nrint

endif

l2=l2+1

ne=nint(xss(l2))

write(nsyso,'(4x,''ne ='',i4)') ne

*d acer.11169

&         xss(l2+ii),xss(l2+ne+ii)

*d acer.11255,11257

write(nsyso,'(4x,''nr ='',i4)') nrint

if (nrint.ne.0) then

write(nsyso,'(4x,''nbt(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

write(nsyso,'(4x,''int(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

endif

l3=l3+1

ne=nint(xss(l3))

write(nsyso,'(4x,''ne ='',i4)') ne

*d acer.11259,11260

e2=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

*d acer.11286,11288

write(nsyso,'(4x,''nr ='',i4)') nrint

if (nrint.ne.0) then

write(nsyso,'(4x,''nbt(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

write(nsyso,'(4x,''int(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

endif

l3=l3+1

ne=nint(xss(l3))

write(nsyso,'(4x,''ne ='',i4)') ne

*d acer.11290,11291

e2=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

*i acer.11311

c

c              ***law=61

else if (law.eq.61) then

nrint=nint(xss(l3))

write(nsyso,'(4x,''nr ='',i4)') nrint

if (nrint.ne.0) then

write(nsyso,'(4x,''nbt(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

write(nsyso,'(4x,''int(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

endif

l3=l3+1

ne=nint(xss(l3))

write(nsyso,'(4x,''ne ='',i4)') ne

do ie=1,ne

e2=xss(ie+l3)

loci=nint(xss(ie+ne+l3)+dlwh-1)

intt=mod(nint(xss(loci)),10)

nd=nint(xss(loci)/10)

nn=nint(xss(loci+1))

loci=loci+1

write(nsyso,'(/6x,'' incident energy = '',

&                 1p,e14.6,''   intt ='',i2,''    nd ='',i4,

&                 ''    np ='',i3)') e2,intt,nd,nn

do ip=1,nn

locj=nint(xss(ip+3*nn+loci)+dlwh-1)

intmu=nint(xss(locj))

nmu=nint(xss(locj+1))

write(nsyso,'(/

&                    6x,'' secondary energy = '',1p,e14.6/

&                    6x,''              pdf = '',e14.6/

&                    6x,''              cdf = '',e14.6/

&                    6x,''            intmu = '',i8/

&                    6x,''              nmu = '',i8/

&               ''         cosine           pdf           cdf'',

&               ''        cosine           pdf           cdf''/

&               ''   ------------  ------------  ------------'',

&               ''  ------------  ------------  ------------'')')

&                    xss(ip+loci),xss(ip+nn+loci),

&                    xss(ip+2*nn+loci),intmu,nmu

do imu=1,nmu,2

if (imu.eq.nmu) then

write(nsyso,'(1x,1p,3e14.6)')

&                          xss(locj+1+imu),xss(locj+1+nmu+imu),

&                          xss(locj+1+2*nmu+imu)

else

write(nsyso,'(1x,1p,6e14.6)')

&                          xss(locj+1+imu),xss(locj+1+nmu+imu),

&                          xss(locj+1+2*nmu+imu),xss(locj+1+imu+1),

&                          xss(locj+1+nmu+imu+1),

&                          xss(locj+1+2*nmu+imu+1)

endif

enddo

enddo

enddo

*d acer.11333,11335

write(nsyso,'(4x,''nr ='',i4)') nrint

if (nrint.ne.0) then

write(nsyso,'(4x,''nbt(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

write(nsyso,'(4x,''int(i=1,nr) = '',20i5)')

&                 (nint(xss(l3+ii)),ii=1,nrint)

l3=l3+nrint

endif

l3=l3+1

ne=nint(xss(l3))

write(nsyso,'(4x,''ne ='',i4)') ne

*d acer.11337,11339

e2=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

intmu=nint(xss(loci))

*i acer.12617

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

*i acer.12619

if (nr.gt.0) then

n=2*nr

do jj=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

*i acer.12791

else if (law.eq.61) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.ne.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

if (nout.ne.1) np=nint(xss(l))

if (nout.eq.1) np=iss(l)

call typen(l,nout,1)

l=l+1

n=3*np

do k=1,n

call typen(l,nout,2)

l=l+1

enddo

do k=1,np

call typen(l,nout,1)

l=l+1

enddo

do k=1,np

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nmu=nint(xss(l))

if (nout.eq.1) nmu=iss(l)

call typen(l,nout,1)

l=l+1

nw=3*nmu

do kk=1,nw

call typen(l,nout,2)

l=l+1

enddo

enddo

enddo

*d acer.18174

locj=nint(xss(j+3*nn+loci)+dlw-1)

*d acer.18179

cc=xss(locj+1+2*nmu+k)

*d acer.18353

j=nint(xss(l3))

if (j.ne.0) then

l3=l3+2*j

endif

l3=l3+1

ne=nint(xss(l3))

*d acer.18355,18356

e=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

*d acer.18384

j=nint(xss(l3))

if (j.ne.0) then

l3=l3+2*j

endif

l3=l3+1

ne=nint(xss(l3))

*d acer.18386,18387

e=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

*d acer.18424

j=nint(xss(l3))

if (j.ne.0) then

l3=l3+2*j

endif

l3=l3+1

ne=nint(xss(l3))

*d acer.18426,18427

e=xss(l3+ie)

loci=nint(xss(l3+ne+ie))+dlwh-1

*d acer.18449

locj=nint(xss(j+3*nn+loci)+dlwh-1)

*d acer.18454

cc=xss(locj+1+2*nmu+k)

*d acer.18459

&                          '' at'',1p,e14.6,'' ->'',e13.6,e14.6)')

*ident up10

*/ leapr -- 13jun00

*/  fix two incorrect constants in leapr.  one affects cases with

*/  diffusive effects, and it has been incorrect since njoy97.0

*/  (oct 97).  the other affects cold hydrogen calculations, and it

*/  has been incorrect since njoy97.53 (dec98).

*d leapr.1186

data c0/.125d0/

*d leapr.1864

data amassh/3.3465d-24/

*ident up11

*/ acer -- 26jun00

*/  fix an error in determinining which reactions have to be

*/  converted into law=7 format when using newfor=0.  because of

*/  overzealous code cleanup, acer is trying to convert sections

*/  with the kalbach representation in addition to sections with

*/  tabulated angular distributions.

*d acer.2324,2330

do while(nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

if (lf.eq.6) then

call contio(nin,0,0,a(iscr),nb,nw)

else if (lf.eq.1.or.lf.eq.2.or.lf.eq.5) then

call tab2io(nin,0,0,a(iscr),nb,nw)

lang=l1h

if (dzap.le.test.and.lf.eq.1.and.lang.ne.2) new6=1

ne=n2h

do ie=1,ne

call listio(nin,0,0,a(iscr),nb,nw)

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

enddo

else if (lf.eq.7) then

call tab2io(nin,0,0,a(iscr),nb,nw)

ne=n2h

do ie=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

nmu=n2h

do imu=1,nmu

call tab1io(nin,0,0,a(iscr),nb,nw)

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

enddo

enddo

endif

*/ acer -- 26jun00

*/  during the cleanup of the topfil routine, the logic to process

*/  sections of file 6 using law=2 (two-body distributions) into

*/  equally probable bins for newfor=0 was omitted.  this shows up

*/  for evaluations that use mf6/mt51, etc., to represent inelastic

*/  levels.

*d acer.2379

if (lf.eq.1) then

*d acer.2387,2388

c                    law=2 for newfor=1 - copy the subsection

else if (lf.eq.2.and.newfor.eq.1) then

*i acer.2394

c                    law=2 for newfor=0 - convert to probability bins

else if (lf.eq.2.and.newfor.eq.0) then

call listio(nin,0,0,a(iscr),nb,nw)

now=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(now),nb,nw)

now=now+nw

enddo

now=now-1

lang=nint(a(iscr+2))

if (lang.eq.0) then

c                          legendre coefficients

call ptleg(nout,a)

else

c                          tabulated angular distribution

do i=iscr,now

a(now+2-i+iscr)=a(now-1+iscr)

enddo

np=nint(a(iscr+7))

a(iscr)=a(iscr+2)

a(iscr+1)=a(iscr+3)

a(iscr+2)=0

a(iscr+3)=0

a(iscr+4)=1

a(iscr+5)=np

a(iscr+6)=np

a(iscr+7)=lang-10

call pttab(ltt,a(iscr),nout)

endif

c                    law=5 for - copy the subsection

else if (lf.eq.5) then

call listio(nin,nout,0,a(iscr),nb,nw)

now=iscr+nw

do while (nb.ne.0)

call moreio(nin,nout,0,a(now),nb,nw)

now=now+nw

enddo

*/ acer -- 26jun00

*/  fix an error in the reaction naming.  it affects mt=44 (n,n2p) and

*/  mt=45 (n,npa).  this problem was introduced in may of 1995.

*/  examples of cases that use these reactions are later releases of

*/  endf/b-vi al-27.

*d acer.11415,11416

&  '(n,x)     ', '(n,2np)   ', '(n,3np)   ', '(n,x)     ',

&  '(n,n2p)   ', '(n,npa)   ', '(n,2/2*1) ', '(n,2/2*2) ',

*/ acer -- 26jun00

*/  add missing external statement.  reported by bokyun seo (kaeri)

*i acer.3250

external error

*/ acer -- 26jun00

*/  add missing line for the sequential (n,2n) reactions for be-9.

*/  this line was accidentally removed in njoy 94.19 (jan96).  the

*/  error was continued through njoy 97 and 99.  discovered by

*/  bob little (lanl).

*i acer.5102

if (mth.ge.46.and.mth.le.49) s=sigfig(s/2,7,0)

*/ acer -- 26jun00

*/  fix anisotropic photon production (e.g., endf c,n,o)

*d acer.7559

if (lff.le.1) then

*ident up12

*/ njoy -- 27jul00

*/  fix two typographical errors in the 64-bit version of the

*/  slatec math library.  reported by piet de leege (delft).

*d njoy.4617

if (a.ge.(-0.5).or.aeps.ne.0.0) then

*d njoy.4935

gamma=0.9375+csevl(2.*y-1.,gamcs,ngamcs)

*ident up13

*/ reconr -- 12jul00

*/  if a reaction uses histogram interpolation, reconr tries to

*/  change it to linear interpolation by moving each point down by

*/  one in the seventh place and and adding a point higher by one in

*/  the seventh place.  if there is already a point in the evaluator's

*/  grid higher by one in the seventh place, the algorithm gets

*/  confused.  this currently occurs for carbon from release 6 of

*/  endf/b-vi.  the symptom is an infinite loop while processing

*/  mf=12,mt=51.  we found this at los alamos, and skipped over the

*/  problem by temporarily patching the evaluation.  more recently,

*/  it was re-reported by waclaw gudowski, and now we are making a

*/  real fix for the problem.

*i reconr.1830

if (er.lt.(1+small)*enl) go to 255

*ident up14

*/ acer -- 20jul00

*/  acer fails if you run it on a pendf tape that only has the

*/  single reaction mt=2 (elastic).  this can happen for he-4 if you

*/  don't run heatr, thermr, or gaspr first.  found by gudowski.

*d acer.5121

mt=2

*/ acer -- 20jul00

*/  acer fails for mf=6, law=2, lang>0 (angular distribution with

*/  tabulated cosines).  the only known example is mt=51 for pb-208 from

*/  release 6 of endf/b-vi.  found by waclaw gudowski.

*d up11.67

a(now+2-i+iscr)=a(now-i+iscr)

*/ acer -- 21jul00

*/  an error was included in up9, which added a capability to handle

*/  anisotropic charged-particle emission represented using legendre

*/  polynomials.  the update disabled the case of isotropic

*/  charged-particle emission, which occurs in a number of important

*/  materials from release 6 of endf/b-vi.  the symptom is a serious

*/  clobbering of the ace file, such that it cannot even be read into

*/  mcnp or even printed using acer.  also reported by gudowski.

*d up9.56

else if (lang.eq.1.and.na.gt.0) then

*d up9.100

if (lang.eq.1.and.na.gt.0) then

*ident up15

*/ heatr -- 31jul00

*/  incorrect initial value found by m.mattes (u.stuttgart).

*d heatr.2586

ir=1

*/  increase the allowed number of legendre terms in h6ddx

*/  to handle the new jeff-3t fe-56 evaluation.

*d heatr.3284

dimension cnow(*),p(15)

*i heatr.3292

data nlmax/15/

*i heatr.3315

if (nl.gt.nlmax) call error('h6ddx',

&  'too many legendre terms',' ')

*/ watch for ill-defined vertical segments in distributions.  these

*/ have been seen in zr90 from cendl3 and fe56 from jeff3.  actually,

*/ the evaluations should be fixed to avoid such features, because

*/ we don't really know what y value to select in the vertical

*/ segment.  we choose to just move the second energy of the double

*/ point up a little.  we only print the diagnostic once to keep the

*/ output cleaner, but there could be more than one vertical segment.

*i heatr.3286

external mess

*i heatr.3287

save illdef

*i heatr.3318

illdef=0

*d heatr.3352,3353

x1=cnow(lnow-ncnow)

x2=cnow(lnow)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&                 'vertical segment(s) in distribution',

&                 'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(lll-ncnow)

y2=cnow(lll)

call terp1(x1,y1,x2,y2,ep,tt,lep)

*d heatr.3364,3367

x1=cnow(lnow-ncnow)

x2=cnow(lnow)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&              'vertical segment(s) in distribution',

&              'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(lnow-ncnow+1)

y2=cnow(lnow+1)

call terp1(x1,y1,x2,y2,ep,s,lep)

y1=cnow(lnow-ncnow+2)

y2=cnow(lnow+2)

call terp1(x1,y1,x2,y2,ep,r,lep)

*d heatr.3380

x1=cnow(ii)

x2=cnow(jj)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&           'vertical segment(s) in distribution',

&           'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(ii+1)

y2=cnow(jj+1)

call terp1(x1,y1,x2,y2,ep,s,lep)

*d heatr.3395

call terp1(x1,tii,x2,tjj,ep,t,lep)

*ident up16

*/ groupr -- 31jul00

*/ watch for ill-defined vertical segments in distributions.  these

*/ have been seen in zr90 from cendl3 and fe56 from jeff3.  actually,

*/ the evaluations should be fixed to avoid such features, because

*/ we don't really know what y value to select in the vertical

*/ segment.  we choose to just move the second energy of the double

*/ point up a little.  we only print the diagnostic once to keep the

*/ output cleaner, but there could be more than one vertical segment.

*i groupr.5588

save illdef

*i groupr.5591

external mess

*i groupr.5633

illdef=0

*d groupr.5675,5676

x1=cnow(lnow-ncnow)

x2=cnow(lnow)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&                    'vertical segment(s) in distribution',

&                    'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(lll-ncnow)

y2=cnow(lll)

call terp1(x1,y1,x2,y2,ep,tt,lep)

*d groupr.5688,5691

x1=cnow(lnow-ncnow)

x2=cnow(lnow)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&                 'vertical segment(s) in distribution',

&                 'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(lnow-ncnow+1)

y2=cnow(lnow+1)

call terp1(x1,y1,x2,y2,ep,s,lep)

y1=cnow(lnow-ncnow+2)

y2=cnow(lnow+2)

call terp1(x1,y1,x2,y2,ep,r,lep)

*d groupr.5722

x1=cnow(ii)

x2=cnow(jj)

if (x1.eq.x2.and.lep.gt.1) then

x2=sigfig(x2,6,1)

if (illdef.eq.0) then

call mess('h6ddx',

&              'vertical segment(s) in distribution',

&              'y(x) is ill defined')

illdef=1

endif

endif

y1=cnow(ii+1)

y2=cnow(jj+1)

call terp1(x1,y1,x2,y2,ep,s,lep)

*d groupr.5737

call terp1(x1,tii,x2,tjj,ep,t,lep)

*ident up17

*/ acer -- 31jul00

*/ fix an incorrect index in the law=61 section for the primary

*/ particle.  the effect of this error is to give an incorrect

*/ angular distribution for the energy points with scattering

*/ probability zero (which should be isotropic).  this change

*/ is strictly cosmetic and shouldn't affect any results.

*d acer.6833

a(jscr+5+ia)=0

*/ acer -- 31jul00

*/ we want to use the compact law=4 for isotropic charged particle

*/ distributions, and the more general law=61 for anisotropic cp

*/ distributions.  unfortunately, we can't tell which is which

*/ without reading past the first few energies for some evaluations.

*/ the need for this patch was first noticed by jeff3 fe56.

*i acer.8982

c

c                 ***first check the subsection to see whether

c                 ***the distribution is isotropic or not.

isocp=1

call findf(matd,mf,mt,nin)

call contio(nin,0,0,a(iscr),nb,nw)

nk=n1h

ik=0

idone=0

do while (ik.lt.nk.and.idone.eq.0)

ik=ik+1

ll=iscr

lly=ll

call tab1io(nin,0,0,a(ll),nb,nw)

izap=nint(c1h)

awp=c2h

law=l2h

ll=ll+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(ll),nb,nw)

ll=ll+nw

enddo

c

c                    ***if not the desired particle, skip the subsection

if (izap.ne.ip) then

call skip6(nin,0,0,a(iscr),law)

c

c                    ***we only need to check law 1 subsections

else if (law.eq.1) theN

call tab2io(nin,0,0,a(ll),nb,nw)

lang=nint(a(ll+2))

lep=nint(a(ll+3))

ne=nint(a(ll+5))

do ie=1,ne

ll=lld

call listio(nin,0,0,a(ll),nb,nw)

ll=ll+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(ll),nb,nw)

ll=ll+nw

enddo

na=nint(a(lld+3))

if (na.gt.0) isocp=0

enddo

endif

enddo

c

c                 ***go back and process the subsection

*d up9.43

if (law.eq.1.and.lang.eq.1.and.isocp.eq.0)

&                    lawnow=61

if (law.eq.1.and.lang.eq.1.and.isocp.eq.1)

&                    lawnow=4

*i up9.48

if (law.eq.1.and.isocp.eq.1) xss(landh+jp-1)=0

*d acer.9079,9082

*d acer.9085

if (lawnow.eq.4) then

*d up14.23

else if (lawnow.eq.61) then

*d up14.25

if (lawnow.eq.61) then

*ident up18

*/ acer -- 03aug00

*/ some jef, eff, and jeff evaluations contain a redundant reaction

*/ mt=10 that gives the continuum neutron production.  it is

*/ necessary to exclude this reaction from the reconstructed total

*/ cross section and to omit the associated energy-angle distribution.

*/ otherwise, the continuum neutron production will be counted twice.

*i acer.1941

if (mt.eq.10) then

idone=0

call mess('unionx','redundant mt=10 found',

&               'cross section and distribution excluded')

endif

*i acer.2193

&     (mf.eq.6.and.mt.eq.10).or.

*/ acer -- 03aug00

*/ this change can fix an infinite loop during acer plotting

*d acer.22571

if (ep.lt.zero) then

*/ acer -- 03aug00

*/ for file 6 sections with only one subsection, the mt number is

*/ set to zero for the messages about energy-dependent yields.

*/ this is a trivial cosmetic patch and doesn't affect results.

*i acer.6414

if (ikk.eq.nk) idone=1

*/ acer -- 03aug00

*/ this change is needed to handle nubar for jendl-3.2 u-235.  it

*/ was originally made at los alamos in april, but somehow didn't

*/ make it to the official update file.

*d acer.1090

if (int.gt.2) nonlin=1

*ident up19

*/ heatr -- 03aug00

*/ as noted above, some jef, eff, and jeff evaluations use the

*/ redundant mt=10.  this value needs to be excluded from the

*/ heating and damage calculations.

*d heatr.639

else if (mt.ne.10) then

*d heatr.690

else if (mt.ne.10) then

*i heatr.855

if (mt.eq.10) go to 110

*ident up20

*/ acer -- 16aug00

*/ there is an error in processing angular distributions using ltt=3

*/ when newfor=0 (mcnp4b compatibility).  the extra tosend causes the

*/ code to skip over the first reaction after the elastic mf=4.

*/ this leads to a bad tyr=0 value in the ace file, which causes

*/ mcnp to issue a confusing error message about "sabcol," even

*/ when s(alpha,beta) is not being used.  this problem occurs only

*/ when processing the 150-mev evalutions from endf/b-vi.6.  it

*/ is probably best to use release 5 with mcnp4b anyway.  the

*/ release 5 and 6 data are identical below 20 mev.

*d acer.2292

*/ acer -- 16aug00

*/ the code is finding the wrong value for the lct parameter (lab

*/ or cm frame) when processing file 4 angular distributions if

*/ the section is fully isotropic.  this can result in an incorrect

*/ value for the ace tyr parameter, which can result in an apparent

*/ error from sabcol, even with no s(alpha,beta) data in the problem.

*/ this problem was introduced while the njoy97 coding was being

*/ converted to block structuring.

*d acer.5342

*i acer.5359

lct=nint(a(iscr+3))

*d acer.5361

*/ acer -- 16aug00

*/ the consistency check for incorrect reference frame should take

*/ place for isotropic distributions also.  sometimes, this check is

*/ not a real error.  users should check the evaluation to see if the

*/ reference frame is really as intended by the evaluator.  as fixed,

*/ this check would have found the two problems above!

*d acer.17785

if (na.ge.0) then

*/ acer-- 16aug00

*/ we are not currently handling law=5 for energy distributions.

*/ this occurs for u-233 fission from jef-2.2.  the evaluation can

*/ be patched by converting the lf=5 part of the distribution to

*/ lf=1, which is sampled much better by mcnp using cummulative

*/ probability distributions anyway.

*i acer.6098

call error('acelf5','sorry. acer cannot handle lf=5.',

&        'you will have to patch the evaluation to use lf=1.')

*/ acer -- 16aug00

*/ there are some additional places where skip6 should be skip6a.

*/ see up6 above.  this shows up for endf be-9 with newfor=1.

*d acer.8066

external error,findex,skip6a,contio,listio,tab1io,moreio,tab2io

*d acer.8289

call skip6a(nin,0,0,a(iscr),law)

*d acer.8880

call skip6a(nin,0,0,a(iscr),law)

*d up17.42

call skip6a(nin,0,0,a(iscr),law)

*d acer.9004

call skip6a(nin,0,0,a(iscr),law)

*d acer.9027

call skip6a(nin,0,0,a(iscr),law)

*d acer.9725

call skip6a(nin,0,0,a(iscr),law)

*/ acer -- 16aug00

*/ there is an error in the law=7 part of up11.  this shows up

*/ when processing endf be-9 using newfor=0

*d up11.29

call tab2io(nin,0,0,a(iscr),nb,nw)

*/ acer -- 16aug00

*/ there is an error in the new skip6a routine introduced by up6

*/ that shows up when processing sections with law=7 with newfor=0.

*d up6.69

nmu=nint(a(4))

*/ acer -- 16aug00

*/ missing initialization in ptlegc (this could affect incident

*/ charged particles on some systems).

*i acer.2217

dco=0

*ident up21

*/ groupr -- 28sep00

*/ the self-shielded cross sections are not being printed out

*/ correctly for the reactions, but total is ok.  the gendf

*/ file is ok, so libraries made with njoy99 are ok.

*d groupr.3613

call a10(ans(il,i,2),field(i))

*ident up22

*/ reconr -- 28sep00

*/ add capability to handle the new extension to the reich-moore

*/ resonance format that uses the sign of aj to designate which

*/ channel spin to use for a particular resonance.  based on

*/ coding provided by nancy larson, ornl.

*d reconr.2828,2942

c

c           ***loop over possible channel spins

kchanl=0

idone=0

do while (kchanl.lt.2.and.idone.eq.0)

kchanl=kchanl+1

inow=inowb

kpstv=0

kngtv=0

c              initialize matrix

do j=1,3

do i=1,3

s(j,i)=0

r(j,i)=0

enddo

enddo

c

c              ***loop over resonances

inow=inow+6

in=inow+nrs*6

do i=1,nrs

aj=abs(a(inow+1))

c                 select only resonances with current j value

if (abs(aj-ajc).le.quar) then

if (a(inow+1).lt.zero) kngtv=kngtv+1

if (a(inow+1).gt.zero) kpstv=kpstv+1

iskip=0

if (kchanl.eq.1.and.a(inow+1).lt.zero) iskip=1

if (kchanl.eq.2.and.a(inow+1).gt.zero) iskip=1

if (iskip.eq.0) then

c                       retrieve parameters

er=a(inow)

gn=a(inow+2)

gg=a(inow+3)

gfa=a(inow+4)

gfb=a(inow+5)

per=a(in+1)

c                       gc=a(in+2)

a1=sqrt(gn*pe/per)

a2=0

if (gfa.ne.zero) a2=sqrt(abs(gfa))

if (gfa.lt.zero) a2=-a2

a3=0

if (gfb.ne.zero) a3=sqrt(abs(gfb))

if (gfb.lt.zero) a3=-a3

c                       compute energy factors

diff=er-e

den=diff*diff+quar*gg*gg

de2=haf*diff/den

gg4=quar*gg/den

c                       calculate r-function, or

c                       calculate upper triangular matrix terms

r(1,1)=r(1,1)+gg4*a1*a1

s(1,1)=s(1,1)-de2*a1*a1

if (gfa.ne.zero.or.gfb.ne.zero) then

r(1,2)=r(1,2)+gg4*a1*a2

s(1,2)=s(1,2)-de2*a1*a2

r(1,3)=r(1,3)+gg4*a1*a3

s(1,3)=s(1,3)-de2*a1*a3

r(2,2)=r(2,2)+gg4*a2*a2

s(2,2)=s(2,2)-de2*a2*a2

r(3,3)=r(3,3)+gg4*a3*a3

s(3,3)=s(3,3)-de2*a3*a3

r(2,3)=r(2,3)+gg4*a2*a3

s(2,3)=s(2,3)-de2*a2*a3

gf=1

endif

endif

endif

inow=inow+ncyc

in=in+3

enddo

c              ***take care of extra channel spin as defined

c              ***by the sign of aj:

c              *** kkkkkk = 0 => do not add anything in here

c              *** kkkkkk = 1 => add resonance contribution but

c              ***  not extra hard-sphere

c              *** kkkkkk = 2 => add resonance plus hard-sphere

c              ***  phase shift contribution

kkkkkk = 0

if (kchanl.eq.1) then

if (kpstv.gt.0) then

if (kngtv.eq.0) then

if (jj.gt.jjl.and.jj.lt.numj) then

kkkkkk=2

else

kkkkkk=1

endif

else if (kngtv.gt.0) then

kkkkkk=1

endif

else if (kpstv.eq.0) then

if (kngtv.eq.0) then

if (jj.gt.jjl.and.jj.lt.numj) then

kkkkkk=2

else

kkkkkk=1

endif

else if (kngtv.gt.0) then

kkkkkk=0

endif

endif

else if (kchanl.eq.2) then

if (kpstv.gt.0) then

if (kngtv.eq.0) then

else if (kngtv.gt.0) then

kkkkkk=1

endif

else if (kpstv.eq.0) then

if (kngtv.eq.0) then

else if (kngtv.gt.0) then

if (jj.gt.jjl.and.jj.lt.numj) then

kkkkkk=2

else

kkkkkk=1

endif

endif

endif

endif

if (kkkkkk.ne.0) then

c                 ***r-matrix path -- make symmetric matrix

if (gf.ne.zero) then

r(1,1)=uno+r(1,1)

r(2,2)=uno+r(2,2)

r(3,3)=uno+r(3,3)

r(2,1)=r(1,2)

s(2,1)=s(1,2)

r(3,1)=r(1,3)

s(3,1)=s(1,3)

r(3,2)=r(2,3)

s(3,2)=s(2,3)

c                    invert the complex matrix

call frobns(r,s,ri,si)

c                    fission term for r-matrix path

t1=ri(1,2)

t2=si(1,2)

t3=ri(1,3)

t4=si(1,3)

termf=four*gj*(t1*t1+t2*t2+t3*t3+t4*t4)

u11r=p1*(two*ri(1,1)-uno)+two*p2*si(1,1)

u11i=p2*(uno-two*ri(1,1))+two*p1*si(1,1)

termt=two*gj*(uno-u11r)

termn=gj*((uno-u11r)**2+u11i**2)

c                 ***r-function path

else

dd=r(1,1)

rr=uno+dd

ss=s(1,1)

amag=rr**2+ss**2

rri=rr/amag

ssi=-ss/amag

uur=p1*(two*rri-uno)+two*p2*ssi

uui=p2*(uno-two*rri)+two*p1*ssi

if (abs(dd).lt.small.and.

&                 abs(phid).lt.small) then

xx=2*dd

xx=xx+2*(dd*dd+ss*ss+phid*phid+p2*ss)

xx=xx-2*phid*phid*(dd*dd+ss*ss)

xx=xx/amag

termt=two*gj*xx

termn=gj*(xx**2+uui**2)

else

termt=two*gj*(uno-uur)

termn=gj*((uno-uur)**2+uui**2)

endif

termf=0

endif

c

c                 ***cross sections contributions

if (kkkkkk.eq.2) then

termn=termn+two*gj*(1-p1)

termt=termt+two*gj*(1-p1)

endif

termg=termt-termf-termn

sigp(2)=sigp(2)+termn

sigp(4)=sigp(4)+termg

sigp(3)=sigp(3)+termf

sigp(1)=sigp(1)+termt

endif

enddo

*ident up23

*/ gaminr -- 28sep00

*/  allow for up to 400 groups (added by request)

*d gaminr.78

common/groupg/igg,ngg,egg(400)

*d gaminr.87

dimension a(250000)

*d gaminr.91

dimension ng2s(400),ig2s(400)

*d gaminr.455

common/groupg/igg,ngg,egg(400)

*d gaminr.602

data ngmax/400/

*d gaminr.521

common/groupg/igg,ngg,egg(400)

*d gaminr.1138

common/groupg/igg,ngg,egg(400)

*ident up24

*/ dtfr -- 28sep00

*/  allow for up to 400 groups (added by request)

*d dtfr.105,107

common/dgrpn/egn(400),ngn

common/dgrpg/egg(400),ngg

common/dstore/a(20000),sig(200000)

*d dtfr.110,111

dimension spect(400)

dimension fcap(400),ffis(400)

*d dtfr.114

data nwamax/20000/, nwsmax/200000/

*d dtfr.928

common/dgrpn/egn(400),ngn

*d dtfr.932

common/dstore/x(3500),y(3500),z(1000),a(212000)

*d dtfr.1262

common/dgrpn/egn(400),ngn

*d dtfr.1409,1410

common/dgrpn/egn(400),ngn

common/dgrpg/egg(400),ngg

*d viewr.1294

dimension lll(400)

*ident up25

*/ groupr -- 11oct00

*/  fix the section that reduces the number of sig figs in getdis.

*/  it was only acting on the in-group probabilities.  this helps

*/  to make the results for elastic and discrete inelastic matrices

*/  the same on different machines.  the basic idea is that these

*/  numbers are obtained by subtraction of numbers on the order of

*/  unity, so any results less than about 1e-7 are just random

*/  numbers and can be removed.

*d groupr.6637,6642

ndig=7

fact=ten**ndig

do il=1,nl

do ii=1,ng

iii=nint(fact*ff(il,ii)+ten**(ndig-11))

ff(il,ii)=iii/fact

enddo

enddo

*/ groupr -- 12oct00

*/  change the size of common groupg to agree with the changes

*/  made in gaminr above.

*d groupr.229

common/groupg/igg,ngg,egg(400)

*d groupr.773

common/groupg/igg,ngg,egg(400)

*d groupr.1919

common/groupg/igg,ngg,egg(400)

*d groupr.3075

common/groupg/igg,ngg,egg(400)

*d groupr.4275

common/groupg/igg,ngg,egg(400)

*d groupr.7780

common/groupg/igg,ngg,egg(400)

*ident up26

*/ acer -- 12oct00

*/  the current coding sometimes gets the threshold for charged

*/  particle production off by one point.

*i acer.8075

data delt/1.d-10/

*i acer.8082

data delt/1.e-10/

*d acer.8166

do while (xss(esz+it-1).lt.thresh*(1-delt))

*ident up27

*/ dtfr -- 27oct00

*/  fix problem with finding right material and temperature

*/  on the pendf tape.  the goto loop was not translated correctly!

*d dtfr.220

idone=0

do while (idone.eq.0)

*i dtfr.239

else

idone=1

*/ dtfr -- 27oct00

*/  fix error made in up24

*d up24.21

common/dgrpg/egg(400),ngp

*ident up28

*/ acer -- 05nov00

*/  the pointer into the a array is not being correctly incremented

*/  for the "call moreio" line.  this only affects the new JEFF

*/  evaluation for beryllium, which has exceptionally detailed

*/  angulur tabulations.  found by fischer (fzk).

*i acer.2439

l=l+nw

*/  fix an indexing error in adjusting the normalization and

*/  precision for the pdf of angular distributions for law67 charged

*/  particle production that causes the pdf to be the same as the

*/  cdf.  this problem shows up for beryllium (n,2n) alpha production

*/  in endf/b-vi, for example.  identified by konno (jaeri).

*d acer.8864

&                          sigfig(renorm*xss(next+1+nx+ix),7,0)

*ident up29

*/ ccccr -- 05nov00

*/  the pointer in the e array for moreio is wrong.  the result of

*/  this is that larger group structures cannot be handled correctly

*/  for delayed neutrons.  found by broeders (karlsruhe).

*d ccccr.3140

call moreio(nin,0,0,e(loc),nb,nw)

*ident up30

*/ heatr -- 05nov00

*/  the insert of the data value for nlmax was incorrectly done into

*/  the "sw" conditional block instead of after the conditional

*/  block was complete.  thus, it was only available to 32-bit

*/  versions of the code.  this was discovered by deleege (delft)

*/  when running in 64-bit mode on a vax/alpha.

*d up15.11

*i heatr.3298

data nlmax/15/

*ident up31

*/ groupr -- 05nov00

*/  fix two problems with the ltt3 option for 150 mev evaluations.

*/  the incorrect index for the c array leads to findex problems

*/  caused by clobbering the index for the dynamic storage system.

*/  you also have to make sure that the "over" option that allows

*/  getfle to extrapolate to energies slightly higher than the

*/  upper limit of the table doesn't act at the break between

*/  the two energy ranges with ltt3.  this problem was reported

*/  by wienke (sck-cen).

*d groupr.6838

if (nne.eq.ne.and.e.lt.over*ehi) then

if (ltt3.eq.3.and.lttn.eq.1) go to 210

go to 300

endif

*d groupr.6850,6851

call tab2io(nin,0,0,c(ifls),nb,nwc)

ne=nint(c(ifls+5))

*ident up32

*/ reconr -- 05nov00

*/  some fission products from the jendl-3.2 library include

*/  an unresolved resonance range with no corresponding resolved

*/  range.  trkov (iaea) proposed the following fix.

*i reconr.672

if (eresr.lt.eresl) eresr=eresl

*ident up33

*/ gaminr -- 18jan01

*/  the photoatomic group cross sections are not printed out

*/  correctly for a p-order greater than 5.

*d gaminr.1075

&              write(nsyso,'(13x,1p,6a11)') (field(i),i=7,nl)

*ident up34

*/ groupr -- 29jan01

*/  need more storage in groupr to handle mt=91 for am243 from

*/  endf/b-vi release 5, which goes to 30 mev.  the symptom was

*/  "storage exceeded" from cm2lab.

*d groupr.248

dimension a(150000)

*d groupr.273

iamax=150000

*ident up35

*/ groupr -- 08feb01

*/  when we increased the common block for photon group structures

*/  to allow as many as 400 groups (see up25), we forgot to update

*/  the parameter ngmax.  this causes a "too many groups" error if

*/  you run with more than 150 gamma groups.

*d groupr.2000

data ngmax/400/

*ident up36

*/ acer -- 08feb01

*/  in up17, we checked for isotropic distributions in order to use

*/  a more compact presentation.  the logic misses one special case,

*/  namely, pb208 from endf/b-vi release 6.

*d up17.41

if (izap.ne.ip.or.law.ne.1) then

*d up17.45

else

*ident up37

*/ reconr -- 09feb01

*/  all through njoy, we have been using 1e10 ev as our idea of

*/  an infinite energy.  progress happens, and red cullen at llnl

*/  is putting out an endf version of the evaluated photon data

*/  library (epdl97), which contains data to 100 gev.  the following

*/  change prevents reconr from going into an infinite loop in the

*/  emerge routine with 100 gev data.

*d reconr.4126

data finity/.99d12/

*d reconr.4130

data finity/.99e12/

*ident up38

*/ njoy -- 09feb01

*/  keep on increasing infinity for the 100 gev data.  the routines

*/  gety1, gety2, and terpa return an "infinite" energy at the end

*/  of the table, and we now increase that to 1e12 ev.  this doesn't

*/  seem to cause any problems in njoy modules (such as groupr) that

*/  still check for return values of 1e10 or more; all the standard

*/  test problems still work fine.

*d njoy.2204

data xbig/1.d12/

*d njoy.2208

data xbig/1.e12/

*d njoy.2418

data xbig/1.d12/

*d njoy.2422

data xbig/1.e12/

*d njoy.2532

data xbig/1.d12/

*d njoy.2536

data xbig/1.e12/

*ident up39

*/ gaminr -- 09feb01

*/  keep on increasing infinity for the 100 gev data.

*d gaminr.106

data emax/1.d12/

*d gaminr.110

data emax/1.e12/

*d gaminr.779

data emax/1.d12/

*d gaminr.782

data emax/1.e12/

*d gaminr.1164

data emax/1.d12/

*d gaminr.1186

data emax/1.e12/

*ident up40

*/ acer -- 23mar01

*/  due to a bad if clause, the contribution to heating from charged

*/  particles is not being included for mf=6, law 3 or 4.  this was

*/  noticed in the run for endf/b-vi be-9 by lanl/x-5.  the errors in

*/  this particular case are quite small because of the small cross

*/  sections for charged-particle emission.  this error will only

*/  effect mcnpx calculations for coupled neutron-proton transport.

*d acer.9220,9231

c                       add in contribution to heating

naa=nint(xss(hpd+1))

do ie=it,nes

e=xss(esz+ie-1)

ss=0

if (ie.ge.iaa) ss=xss(2+k+ie-iaa)

tt=xss(next+1)*(e-xss(next))*ss

xss(hpd+2+naa+ie-it)=xss(hpd+2+naa+ie-it)

&                       +tt

enddo

*ident up41

*/ acer -- 27mar01

*/  the value "nr = 0", implying linear interpolation over all points,

*/  is not printed on the acer output listing for two cases, as reported

*/  by lanl/x-5.  these errors do not affect mcnp results, but the

*/  repair makes the printout for photon yields and energy distributions

*/  match those for other types of data.

*i acer.10808

write(nsyso,'(12x,''nr ='',i4)') m

*d acer.10810

*i acer.10998

write(nsyso,'(12x,''nr ='',i4)') m

*d acer.11000,11002

*ident up42

*/ purr -- 27mar01

*/  remove the timers that are given as each ladder is processed

*/  in order to reduce the number of diffs that show up when

*/  succesive runs are checked for qa purposes using the same

*/  sequence of random numbers.  for lanl/x-5.

*d purr.1746

external fsort,ladr2,fsrch

*d purr.1798

&  ''capture'')') e,spot,dbart,sigx

*d purr.2145,2147

if (iprint.gt.0) write(nsyso,'(i6,1p,4e12.4)')

&  iladr,totf,elsf,fisf,capf

*ident up43

*/ heatr -- 27mar01

*/  the roundup applied to the first energy grid point should

*/  be smaller now that we are routinely working with 7-digit

*/  energies.  the effect if this in current files is that the

*/  first energy in any of the heating and damage reactions is

*/  a little larger than the normal 1e-5.  this shows up as a

*/  zero heating or damage value for the first point in the mcnp

*/  ace files, which is strange looking, but of little significant

*/  impact on real calculations.  reported by lanl/x-5.

*d heatr.425

data rup/1.0000001d0/

*ident up44

*/ acer -- 29mar01

*/  lanl/x-5 has requested that the main container array be increased

*/  in size to allow bigger ace files to be generated. it is also

*/  necessary to increase the i7 length field on the xsdir cards to i8

*/  to accomodate the larger ace files.

*d acer.257

max3=1500000

*d acer.4662

common/xsst/xss(1500000),n3

*d acer.5601

common/xsst/xss(1500000),n3

*d acer.5762

common/xsst/xss(1500000),n3

*d acer.5951

common/xsst/xss(1500000),n3

*d acer.6322

common/xsst/xss(1500000),n3

*d acer.7383

common/xsst/xss(1500000),n3

*d acer.8055

common/xsst/xss(1500000),n3

*d acer.9754

common/xsst/xss(1500000),n3

*d acer.10202

common/xsst/xss(1500000),n3

*d acer.10675

common/xsst/xss(1500000),n3

*d acer.11068

common/xsst/xss(1500000),n3

*d acer.11588

common/xsst/xss(1500000),n3

*d acer.11649

&        '(a10,f12.6,'' filename route'',i2,i4,i8,2i6,1p,e10.3,

*d acer.11653

&        '(a10,f12.6,'' filename route'',i2,i4,i8,2i6,1p,e10.3)')

*d acer.11659

&        '(a13,f12.6,'' file route'',i2,i4,i8,2i6,1p,e10.3,

*d acer.11663

&        '(a13,f12.6,'' file route'',i2,i4,i8,2i6,1p,e10.3)')

*d acer.11689

common/xsst/xss(1500000),n3

*d acer.12854

common/xsst/xss(1500000),n3

*d acer.13452

common/xsst/xss(1500000),n3

*d acer.13591

common/xsst/xss(1500000),n3

*d acer.13771

common/xsst/xss(1500000),n3

*d acer.14170

common/xsst/xss(1500000),n3

*d acer.14274

&     '(a10,f12.6,'' filename route'',i2,2h 1,i8,2i6,1p,e10.3)')

*d acer.14278

&     '(a13,f12.6,'' filename route'',i2,2h 1,i8,2i6,1p,e10.3)')

*d acer.14305

common/xsst/xss(1500000),n3

*d acer.14462

common/xsst/xss(1500000),n3

*d acer.14548

common/xsst/xss(1500000),n3

*d acer.14640

&     '(a10,f12.6,'' filename route'',i2,2h 1,i8,2i6,1p,e10.3)')

*d acer.14644

&     '(a13,f12.6,'' filename route'',i2,2h 1,i8,2i6,1p,e10.3)')

*d acer.14674

common/xsst/xss(1500000),n3

*d acer.15012

common/xsst/xss(1500000),n3

*d acer.15107

common/xsst/xss(1500000),n3

*d acer.15187

&     '(a10,f12.6,'' filename route'',i2,'' 1'',i8,2i6,1p,e10.3)')

*d acer.15191

&     '(a13,f12.6,'' filename route'',i2,'' 1'',i8,2i6,1p,e10.3)')

*d acer.15216

common/xsst/xss(1500000),n3

*d acer.16604

common/xsst/xss(1500000),n3

*d acer.17057

common/xsst/xss(1500000),n3

*d acer.17436

&     '(a10,f12.6,'' filename route'',i2,'' 1'',i8,2i6,1p,e10.3)')

*d acer.17440

&     '(a13,f12.6,'' filename route'',i2,'' 1'',i8,2i6,1p,e10.3)')

*d acer.17459

common/xsst/xss(1500000),n3

*d acer.17727

common/xsst/xss(1500000),n3

*d acer.18534

common/xsst/xss(1500000),n3

*d acer.19545

common/xsst/xss(1500000),n3

*d acer.19817

common/xsst/xss(1500000),n3

*d acer.19934

common/xsst/xss(1500000),n3

*d acer.20164

common/xsst/xss(1500000),n3

*d acer.20610

common/xsst/xss(1500000),n3

*d acer.21222

common/xsst/xss(1500000),n3

*d acer.21815

common/xsst/xss(1500000),n3

*ident up45

*/ acer -- 08apr01

*/  as discovered by jean christophe sublet, sun forte6 f95 is

*/  finiky about opening a scratch file that is already open,

*/  although all other compilers used for njoy thus far were more

*/  accepting.  we just have to be careful to close a unit used

*/  as a scratch file before reusing the unit for another purpose.

*i acer.2082

call closz(nscr)

*ident up46

*/ gaspr -- 09apr01

*/  close another scratch unit.

*i gaspr.838

call closz(nscr1)

*ident up47

*/ acer -- 09apr01

*/  the length published for thermal data files is too long by one

*/  for cases including incoherent elastic scattering.  for endf,

*/  this is poly, h(zrh), and cold solid methane.  discovered by

*/  roberto orsi (enea-bologna).

*d acer.13517

*ident up48

*/ acer -- 09apr01

*/  the landh parameter should be zero (not -1) for isotropic

*/  subsections of mf=6 described using law=3.  this occurs for

*/  the reactions (n,p0) through (n,a0) in be-9 from endf/b-vi.

*/  Noted by bob little (lanl/x-5).

*i acer.9209

if (law.eq.3) xss(landh+jp-1)=0

*ident up49

*/ acer -- 09apr01

*/  the representation for ace law3/33 should use -q instead of

*/  abs(q) in order to handle two-body reactions for isomeric

*/  targets.  this change in the ace specifications was recommended

*/  by bob little (lanl/x-5) after a query by waclaw gudowski.  it

*/  only affects a small number of evaluations.

*d acer.5465

xss(next+9)=sigfig(x*(-q),7,0)

*d acer.8964

xss(next)=sigfig((1+amass)*(-q)/amass,7,0)

*d acer.9167

xss(next)=sigfig((1+amass)*(-q)/amass,7,0)

*d acer.9216

xss(next)=sigfig((1+amass)*(-q)/amass,7,0)

*d acer.16168

xss(nex)=sigfig(-q,7,0)

*d acer.16526

xss(nex)=sigfig(-q,7,0)

*ident up50

*/ acer -- 09apr01

*/  most of the jendl photonuclear evaluations currently available

*/  from http://iaeand.iaea.or.at/photonuclear/ crash with an i/o

*/  error because they use a non-conforming format where mf=6,

*/  mt=201-27 are used to represent particle production.  we are

*/  providing a clearer error message for the user's convenience.

*/  these evaluations cannot be used in njoy or mcnpx in their

*/  current form.

*i acer.15310

if (mfd.eq.6.and.mtd.ge.201.and.mtd.le.207)

&        call error('acephn','mf=6/mt=201-207 not supported.',

&        'does not conform to endf format.')

*ident up51

*/ acer -- 12apr01

*/  add a capability to handle a two-body recoil subsection of mf=6

*/  for photonuclear files.  this may be useful for representing the

*/  photodisintegration of the deuteron with full distributions for

*/  both neutron and proton.  we tested the patch using a modified

*/  version of the g+2H evaluation from JENDL.

*d acer.16011

c

c                    ***special steps for two-body recoil

c                    ***back up to the corresponding law=2 distr.

izarec=0

awprec=0

if (izap.eq.ip.and.law.eq.4) then

izarec=izap

awprec=awp

mf=6

call findf(matd,mf,mt,nin)

call contio(nin,0,0,a(iscr),nb,nw)

call tab1io(nin,0,0,a(iscr),nb,nw)

izap=nint(c1h)

awp=c2h

law=l2h

jscr=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(jscr),nb,nw)

jscr=jscr+nw

enddo

endif

c

c                    ***law2 angular distribution

c                    ***also used for law 4 two-body recoils

if ((izap.eq.ip.and.law.eq.2).or.

&                 (izarec.eq.ip.and.law.eq.2)) then

lld=jscr

*i acer.16030

if (izarec.eq.0) then

awpp=awp

else

awpp=awprec

endif

*i acer.16036

if (izarec.ne.0) then

nl=nint(a(lld+5))

do iil=1,nl

if (mod(iil,2).eq.1) then

a(lld+5+iil)=-a(lld+5+iil)

endif

enddo

endif

*d acer.16104

a(llht+7+2*iie)=(awr-awpp)*(e+q)/awr

*d acer.16354

if (law.ne.1.and.law.ne.2.and.law.ne.4) then

*d acer.16356

&                       'law=2, or law=4 currently')

*i acer.16540

else if (law.eq.4) then

xss(last+1)=33

xss(nex)=0

xss(nex+1)=2

nnr=nint(a(iscr+4))

nnp=nint(a(iscr+5))

xss(nex+2)=sigfig(a(iscr+6+2*nnr)/emev,7,0)

xss(nex+3)=

&                        sigfig(a(iscr+4+2*nnr+2*nnp)/emev,7,0)

xss(nex+4)=1

xss(nex+5)=1

nex=nex+2+2*2

xss(last+2)=nex-dlwp+1

xss(nex)=sigfig(-q,7,0)

xss(nex+1)=sigfig(awr/(1+awr),7,0)

nex=nex+2

*ident up52

*/ acer -- 13apr01

*/  add a capability to handle tabulated sections of File 5 (lf=1)

*/  for photonuclear files.  Such sections are used in the Russian

*/  evaluations for three isotopes of plutonium included in the

*/  iaea photonuclear compilation.  this also fixes a bug in the

*/  storage of fission nubar.  the first point for energy distributions

*/  often has a nonrealistic sharp triangle given for the spectrum.

*/  this can cause problems with the vertical scale for plots

*/  because the emission probabilities get very large for small

*/  ranges of secondary energy.  therefore, we ignore the first

*/  incident energy in determining the vertical scale for the plot.

*d acer.15858,15859

xss(nex+3+j)=sigfig(fnubar(5+2*nr+2*j)/emev,7,0)

xss(nex+3+ne+j)=sigfig(fnubar(6+2*nr+2*j),7,0)

*d acer.16247

if (lf.eq.1) then

call tab2io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

jnt=nint(a(iscr+7))

jnt=mod(jnt,10)

if (jnt.gt.2) jnt=2

if (m.ne.1.or.jnt.ne.2) then

xss(nex)=m

do j=1,m

xss(j+nex)=a(2*j+4+iscr)

jnt=nint(a(2*j+5+iscr))

jnt=mod(jnt,10)

if (jnt.gt.2) jnt=2

xss(j+m+nex)=jnt

enddo

nex=nex+1+2*m

else

xss(nex)=0

nex=nex+1

endif

xss(nex)=n

nexn=nex+n

nexd=nexn+n+1

ne=n

do j=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

e=c2h

xss(nex+j)=sigfig(e/emev,6,0)

xss(nexn+j)=nexd-dlwp+1

m=n1h

n=n2h

jnt=nint(a(iscr+5+2*m))

xss(nexd)=jnt

xss(nexd+1)=n

nexd=nexd+1

xss(nexd+1+2*n)=0

do ki=1,n

ep=a(iscr+4+2*m+2*ki)

ll=iscr+4+2*m+2*ki

xss(ki+nexd)=sigfig(a(ll)/emev,7,0)

xss(ki+n+nexd)=sigfig(a(ll+1)*emev,7,0)

if (xss(ki+n+nexd).lt.rmin) xss(ki+n+nexd)=0

if (ki.gt.1.and.jnt.eq.1) xss(ki+2*n+nexd)=

&                       xss(ki+2*n-1+nexd)+a(ll-1)*(a(ll)-a(ll-2))

if (ki.gt.1.and.jnt.eq.2) xss(ki+2*n+nexd)=

&                       xss(ki+2*n-1+nexd)+((a(ll-1)

&                       +a(ll+1))/2)*(a(ll)-a(ll-2))

enddo

c                       renormalize

renorm=1

if (xss(3*n+nexd).ne.zero)

&                    renorm=1/xss(3*n+nexd)

do ki=1,n

xss(ki+n+nexd)=

&                       sigfig(xss(ki+n+nexd)*renorm,7,0)

xss(ki+2*n+nexd)=

&                       sigfig(xss(ki+2*n+nexd)*renorm,9,0)

enddo

nexd=nexd+3*n+1

enddo

nex=nexd

else if (lf.eq.7.or.lf.eq.9) then

*d acer.22424

do ie=2,ne

*ident up53

*/ groupr -- 11jun01

*/  if the file6 distribution is fully isotropic (law=3), the getfle

*/  routine doesn't realize that when doing a discrete recoil (law=4).

*/  we create a special flag of law=-4 to pass the fact of isotropy

*/  into getfle.  this problem only affects runs that compute a

*/  transfer matrix for the recoil particle when the first particle

*/  emitted is given as totally isotropic (for example, mt=701 for

*/  endf be-9).  the error message is "desired energy above highest

*/  given."  found by dieter leichtle (fzk).

*i groupr.4859

lf=nint(c(l+3))

*i groupr.4860

if (lf.eq.3) law=-4

*i groupr.4869

if (law.eq.-4) go to 194

*i groupr.6786

if (law.eq.-4) iso=1

*ident up54

*/ reconr -- 12jun01

*/  allow for the series of mt numbers 875-891 that can be used

*/  to represent different levels of the (n,2n) reaction in the

*/  same way that 600-649 are used to represent different levels

*/  of the (n,p) reaction.  the code expects that mf=3/mt=16

*/  contains the sum of mt=875 through 891 in the same way that

*/  mt=103 contains the sum of 600-649.  this representation is

*/  used for be-9 for eff-3.1 and jeff-3.0.

*d reconr.1696

if (mth.ge.900) go to 150

*ident up55

*/ heatr -- 12jun01

*/  if mt=875-891 appears in the file, mt=16 is redundant.  this

*/  is analogous to the way mt=107 is redundant if mt=800-850

*/  is present.

*d heatr.412

common/heat4/mt103,mt104,mt105,mt106,mt107,mt16

*i heatr.440

mt16=0

*i heatr.499

if (mtd.ge.875.and.mtd.lt.891) mt16=1

*d heatr.783

common/heat4/mt103,mt104,mt105,mt106,mt107,mt16

*i heatr.865

if (mt.eq.16.and.mt16.gt.0) go to 110

*/  the integration over secondary energy for law 7 in getsix

*/  must allow for histogram interpolation as used in be-9

*/  from eff-3.1.  the effect of this is to get especially

*/  bad particle energies for the discrete neutron in mt=876.

*i heatr.3008

iint=nint(c(l+7))

*d heatr.3020

if (i.gt.1) then

if (iint.eq.1) then

h=h+(xx-xl)*el

else

h=h+(xx-xl)*(en+el)/2

endif

endif

*d heatr.3022

if (i.gt.1) then

if (iint.eq.1) then

d=d+(xx-xl)*fl

else

d=d+(xx-xl)*(fn+fl)/2

endif

endif

*ident up57

*/ acer -- 12jun01

*/  changes to acer needed to support the eff-3.1/jeff-3.0

*/  representation for be-9.  we have to allow for the series

*/  of mt numbers 875-891.  if present, mt=16 is redundant and

*/  must appear after the distributions in the reaction list.

*/  the section for mt=876 has two subsections for neutron

*/  emission.  this problem is handled by the previous update.

*i acer.551

common/ace9/mt16

*i acer.642

mt16=0

*i acer.663

if (mtd.ge.875.and.mtd.le.891) mt16=1

*d acer.1939

&           (iverf.ge.6.and.mt.gt.900)) then

*i acer.4671

common/ace9/mt16

*i acer.4760

if (mt16.gt.0.and.mt.eq.16) nr=nr-1

*d acer.4759

if ((mt.ge.5.and.mt.le.91).or.

&                (mt.ge.875.and.mt.le.899)) then

*i acer.5021

if (mt.gt.91.and.mt.le.849) iskip=1

if (mt16.gt.0.and.mt.eq.16) iskip=1

*d acer.5118,5120

call findf(matd,3,2,nin)

*d acer.5127

if (mt.gt.91.and.mt.le.849) iskip=0

if (mt16.gt.0.and.mt.eq.16) iskip=0

*d acer.9481

renorm=1

if (xss(next+3*npep).ne.zero)

&                          renorm=1/xss(next+3*npep)

*/  add the new reaction names to the mtname routine

*d acer.11389

character*10 hndf(457)

*d acer.11393,11394

character*10 hndf9(50)

character*10 hndf10(7)

character*10 hndf11(1)

*d acer.11403,11404

equivalence (hndf9(1),hndf(400))

equivalence (hndf10(1),hndf(450))

equivalence (hndf11(1),hndf(457))

*i acer.11514

data hndf9/'(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,2n*0)  ',

&  '(n,2n*1)  ', '(n,2n*2)  ', '(n,2n*3)  ', '(n,2n*4)  ',

&  '(n,2n*5)  ', '(n,2n*6)  ', '(n,2n*7)  ', '(n,2n*8)  ',

&  '(n,2n*9)  ', '(n,2n*10) ', '(n,2n*11) ', '(n,2n*12) ',

&  '(n,2n*13) ', '(n,2n*14) ', '(n,2n*15) ', '(n,2n*c)  ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     ',

&  '(n,x)     ', '(n,x)     ', '(n,x)     ', '(n,x)     '/

*d acer.11520,11522

data hndf10/'(n,xn)    ','(n,xgma)  ','(n,xp)    ',

&  '(n,xd)    ','(n,xt)    ','(n,xhe3)  ','(n,xa)    '/

data hndf11(1)/'damage    '/

*d acer.11526,11528

if (i.ge.201.and.i.le.207) i=i+249

if (i.ge.600) i=i-450

if (mt.eq.444) i=457

*d acer.11534

name=hndf(mt+250)

*d acer.11536

name=hndf(457)

*/  need more storage for eff-3.1 be-9

*d up44.8

max3=3000000

*d up44.10

common/xsst/xss(3000000),n3

*d up44.12

common/xsst/xss(3000000),n3

*d up44.14

common/xsst/xss(3000000),n3

*d up44.16

common/xsst/xss(3000000),n3

*d up44.18

common/xsst/xss(3000000),n3

*d up44.20

common/xsst/xss(3000000),n3

*d up44.22

common/xsst/xss(3000000),n3

*d up44.24

common/xsst/xss(3000000),n3

*d up44.26

common/xsst/xss(3000000),n3

*d up44.28

common/xsst/xss(3000000),n3

*d up44.30

common/xsst/xss(3000000),n3

*d up44.32

common/xsst/xss(3000000),n3

*d up44.42

common/xsst/xss(3000000),n3

*d up44.44

common/xsst/xss(3000000),n3

*d up44.46

common/xsst/xss(3000000),n3

*d up44.48

common/xsst/xss(3000000),n3

*d up44.50

common/xsst/xss(3000000),n3

*d up44.52

common/xsst/xss(3000000),n3

*d up44.58

common/xsst/xss(3000000),n3

*d up44.60

common/xsst/xss(3000000),n3

*d up44.62

common/xsst/xss(3000000),n3

*d up44.68

common/xsst/xss(3000000),n3

*d up44.70

common/xsst/xss(3000000),n3

*d up44.72

common/xsst/xss(3000000),n3

*d up44.78

common/xsst/xss(3000000),n3

*d up44.80

common/xsst/xss(3000000),n3

*d up44.82

common/xsst/xss(3000000),n3

*d up44.88

common/xsst/xss(3000000),n3

*d up44.90

common/xsst/xss(3000000),n3

*d up44.92

common/xsst/xss(3000000),n3

*d up44.94

common/xsst/xss(3000000),n3

*d up44.96

common/xsst/xss(3000000),n3

*d up44.98

common/xsst/xss(3000000),n3

*d up44.100

common/xsst/xss(3000000),n3

*d up44.102

common/xsst/xss(3000000),n3

*d up44.104

common/xsst/xss(3000000),n3

*d up44.106

common/xsst/xss(3000000),n3

*ident up58

*/ broadr -- 10jul01

*/  increase the storage area in broadr to reduce paging and make

*/  comparisons between njoy99 and njoy2001 easier.  there will

*/  normally be a small difference in the grids produced by broadr

*/  each time paging takes place, and this makes it hard to compare

*/  files using diff.

*d broadr.113

dimension a(95000)

*d broadr.137

namax=95000

*ident up59

*/ acer -- 20jul01

*/  in charged-particle emission, the first point for energy

*/  distributions often has a nonrealistic sharp triangle given for

*/  the spectrum.  this can cause problems with the vertical scale

*/  incident energy in determining the vertical scale for the plot.

*d acer.21529

do ie=2,ne

*ident up60

*/ reconr -- 24sep01

*/  occasionally, reactions are given with a nonzero cross section

*/  at threshold, even though this violates endf procedures.  reconr

*/  had some logic for handling this that was being overwritten by

*/  another change.  we fix it here by inserting an extra energy

*/  point just above the threshold and zeroing the cross section at

*/  the threshold.  a diagnostic message is provided.  one example

*/  of a place were this occurs is gd158 from endf/b-vi.  reported

*/  by frankle (lanl).

*i reconr.1588

character*40 text

*d reconr.1716,1719

write(text,'(''xsec nonzero at threshold for mt='',i3)') mth

call mess('lunion',text,'adusted using jump in xsec')

*d reconr.1767

er=sigfig(er,7,0)

*d reconr.1783

enl=sigfig(er,7,0)

*d reconr.4204

*/ reconr -- 24sep01

*/  reconr contains some logic that tries to avoid doing work on

*/  very small charged-particle cross sections by defining a

*/  "pseudo-threshold" when the cross section rises to more than

*/  1e-15 barns.  however, this scheme isn't carried out completely,

*/  and it only results in the omission of the threshold energy for

*/  reactions that have less than this cross section just above

*/  the threshold.  this effect shows up for the (n,n't) reaction

*/  mt=33 for cd-110 from endf/b-vi.4.  at the request of bob

*/  little (lanl), we are changing the constant "ssmall" that

*/  triggers this effect to a smaller number.  in the long term,

*/  we should reconsider this logic.

*d reconr.1601

ssmall=1.d-30

*d reconr.1614

ssmall=1.e-30

*ident up61

*/ acer -- 25sep01

*/  kisako kazuaki (sumimoto) has observed that the common variable

*/  coeff in eval is not set.  actually, eval is not really used in

*/  tabize anymore.  it is just leftover as an intialization for a(iy).

*/  the only other place it is used is in islin2, and islin2 is not

*/  called anymore!  This update removes these leftover remnants.

*d acer.1019

*d acer.1022

external loada,finda,error,sigfig

*d acer.1128

a(iy)=0

*d acer.1216,1263

*/  kazuaki also noticed that the photoatomic heating value was

*/  being stored in ev instead of mev and that the atomic number

*/  aw0 was not being set.

*i acer.14730

aw0=c2h

*d acer.14839

xss(lhnm-1+i)=heat/emev

*ident up62

*/ purr -- 28sep01

*/  lanl group x-5 has noted that the conditional heating cross

*/  section in the mcnp probability tables is not quite what they

*/  expected.  we change the calculation here to get results that

*/  are consistently given as eV/reaction for lssf=0 and fluctuation

*/  factors for lssf=1.

*i purr.79

zero=0

*d purr.454,458

if (sigu(2,1,1).ne.zero) h=h*a(n1+j+2*nbin)/sigu(2,1,1)

*d purr.461,465

if (sigu(3,1,1).ne.zero) h=h*a(n1+j+3*nbin)/sigu(3,1,1)

*d purr.468,472

if (sigu(4,1,1).ne.zero) h=h*a(n1+j+4*nbin)/sigu(4,1,1)

*d purr.477

if (a(n1+j+nbin).ne.zero) a(l)=a(l)/a(n1+j+nbin)

*ident up64

*/ acer -- 07dec01

*/  there was a mistake introduced with up57 that only affects

*/  64-bit compiles (when "*set sw" is not used).

*/ *d up56.16,17

*/ *i acer.2135

*/       zero=0

*/       one=1

*ident up65

*/ groupr -- 10dec01

*/  fix groupr to handle radionuclide production using the new

*/  endf file 8 and data from eaf2001.

*d groupr.501,502

if (mfd.gt.36.and.mfd.lt.10000000) go to 381

*d groupr.516

if (mfd.gt.10000000) izam=mod(mfd,10000000)

*d groupr.525

if (mfd.le.10000000) go to 405

*d groupr.621,622

if (mfd.lt.1000000) then

write(nsyso,'('' for mf'',i3,'' and mt'',i3,1x,15a4)')

&           mfd,mtd,(mtname(i),i=1,15)

else

mfdn=mfd/10000000

jzam=mod(mfd,10000000)

if (mfdn.eq.1) then

write(nsyso,

&              '('' for mf3 mt'',i3,'' zam'',i8,1x,15a4)')

&              mtd,jzam,(mtname(i),i=1,15)

else if (mfdn.eq.2) then

write(nsyso,

&              '('' for mf3*mf6 mt'',i3,'' zam'',i8,1x,15a4)')

&              mtd,jzam,(mtname(i),i=1,15)

else if (mfdn.eq.3) then

write(nsyso,

&              '('' for mf3*mf9 mt'',i3,'' zam'',i8,1x,15a4)')

&              mtd,jzam,(mtname(i),i=1,15)

else if (mfdn.eq.4) then

write(nsyso,

&              '('' for mf10 mt'',i3,'' zam'',i8,1x,15a4)')

&              mtd,jzam,(mtname(i),i=1,15)

endif

endif

*i groupr.633

if (mfd.gt.10000000) mfh=3

*i groupr.657

if (mfd.gt.10000000) mfh=3

*d groupr.910

mfd=mf10i(ir)

*d groupr.1163

else if (mfd.gt.10000000) then

*d groupr.3123

if (mfd.ne.3.and.mfd.ne.8.and.mfd.ne.18.and.mfd.lt.10000000) then

*d groupr.3857

if (mft.eq.9.or.mft.eq.10) lfn=nint(a(iyld+3))

if (mft.eq.6) lfn=nint(a(iyld+2))

*d groupr.3862,3871

call skip6(itape,0,0,a(loc),law)

*d groupr.3859

if (mft.gt.6.and.izn.eq.0.and.lfs.eq.lfn) go to 180

*d groupr.3975,3982

if (mf.eq.10) then

nfs=n1h

jfs=-1

do i=1,nfs

call tab1io(nsig,0,0,a(isig),nb,nw)

if (l2h.eq.lfs) jfs=i

do while (nb.ne.0)

call moreio(nsig,0,0,a(isig),nb,nw)

enddo

enddo

if (jfs.lt.0) call error('getsig',

&        'desired lfs not found',' ')

nskip=jfs-1

call skiprz(nsig,-1)

call findf(matd,mf,mt,nsig)

call contio(nsig,0,0,a(isig),nb,nw)

if (nskip.gt.0) then

do i=1,nskip

call tab1io(nsig,0,0,a(isig),nb,nw)

do while (nb.ne.0)

call moreio(nsig,0,0,a(isig),nb,nw)

enddo

enddo

endif

*d groupr.4345

if (mfd.eq.12.or.(mfd.gt.20000000.and.mfd.lt.40000000))

*ident up66

*/ groupr -- 12feb02

*/  if you mix automatic reactions with manual reactions where

*/  the mtname string is not given, the mtname on the manual

*/  reaction will have whatever string was left from the previous

*/  case.  we fix that here.

*d groupr.507

*/ groupr -- 13feb02

*/  there is an error in the calculation of the kalbach a factor

*/  for the photonuclear case.  it is necessary to convert e to

*/  mev for this formula.  the symptom is results for a that are

*/  so large that sinh(a) overflows with a floating point error.

*d groupr.5980

bb=bb*sqrt((tomev*e)/(2*emc2))*fact

*ident up67

*/ matxsr -- 12feb02

*/  add photonuclear capability

*i matxsr.30

c     *   ngen8     photonuclear data from groupr (default=0)          *

*d matxsr.210

cd                     gscat     gamma scattering (atomic)             -

cd                     gg        gamma scattering (photonuclear)       -

*d matxsr.392

&  nscrt5,nscrt6,nscrt7,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*d matxsr.422

ngen8=0

read(nsysi,*)

&  ngen1,ngen2,nmatx,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*d matxsr.433,434

&  '' incident alpha unit .................. '',i10/

&  '' photonuclear unit .................... '',i10)')

&  ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*d matxsr.441

nscrt8=17

*i matxsr.448

call openz(ngen8,0)

*i matxsr.475

call closz(ngen8)

*d matxsr.495

&  nscrt5,nscrt6,nscrt7,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*d matxsr.892

&  nscrt5,nscrt6,nscrt7,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*i matxsr.909

character*8 hgg

*d matxsr.917

data hgsct/'gscat '/, hgg/'gg    '/, hnthr/'ntherm'/

*i matxsr.945

if (nin.eq.0) nin=ngen8

*d matxsr.1012

if (hprt(ip1).eq.hgm) nin=ngen8

if (hprt(ip1).eq.hgm.and.htyp.eq.hgsct) nin=ngen2

*d matxsr.1027,1028

if (hprt(ip2).eq.hgm.and.htyp.ne.hgg) mfv=13

if (hprt(ip1).eq.hgm.and.htyp.eq.hgsct) mfv=23

*i matxsr.1035

if (hprt(ip2).eq.hgm.and.htyp.eq.hgg) mfm=16

*d matxsr.1478

&  nscrt5,nscrt6,nscrt7,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*d matxsr.1809

&  nscrt5,nscrt6,nscrt7,ngen3,ngen4,ngen5,ngen6,ngen7,ngen8

*ident up68

*/ reconr -- 18apr02

*/  the name "pi" is being used for both the imaginary part of

*/  p and the pi constant.  the former is changed to "pim" as

*/  used in the version of this subroutine in purr.  the symptom

*/  is a floating point error when sqrt(pi) is calculated with

*/  pi changed to a negative value.

*d reconr.4868

pim=aimw

*d reconr.4873

if (abs(aimw-pim).ge.eps) go to 380

*d reconr.4908

pim=aimw

*d reconr.4912

if (abs(aimw-pim).ge.eps) go to 470

*/  allow for more digits in the temperature printout to

*/  handle the usage of reconr being made for eaf-2001.  the

*/  temperature field is not being used for resonance

*/  reconstruction but only passed to the output file for

*/  later use.

*d reconr.348

&  '' reconstruction temperature ........... '',f10.2,''k''/

*ident up69

*/ acer -- 07dec01

*/  add a capability to generate fluorescence data for mcnp using

*/  the existing cashwell-everett format with new numbers obtained

*/  from the endf versions of eadl and epdl.  the data produced with

*/  this method should give reasonable results for transport and

*/  heating for energies above 1 kev.  the new evaluations allow

*/  for lower incident photon energies and for more detail in photon

*/  and electron distributions from photoabsorption, and future

*/  versions of njoy and mcnp can take advantage of this.

*d acer.66

c     * data.  the input photoatomic data is mounted on nendf.         *

c     * fluorescence data can be generated from atomic relaxation      *

c     * data in endf format mounted on npend.                          *

*i acer.186

c     *             photoatomic data on nendf                          *

c     *             atomic relaxation data on npend                    *

*d acer.428

call acepho(nendf,npend)

*d acer.14651

subroutine acepho(nin,nlax)

*d acer.14690

data emax/1.01d11/

*d acer.14702

data emax/1.01e11/

*i acer.14780

c

c     ***set number of fluorescence lines

iz=matd/100

if (iz.lt.12) then

nflo=0

else if (iz.lt.20) then

nflo=2

else if (iz.lt.31) then

nflo=4

else if (iz.lt.37) then

nflo=5

else

nflo=6

endif

*d acer.14786

lhnm=jflo+4*nflo

*d acer.14843

c     ***for fluorescence photons

*d acer.14845,14846

if (nlax.eq.0) then

call mess('acepho','no atomic relaxation data',

&     'fluorescence data not processed')

else if (nflo.gt.0) then

call alax(nin,nlax,xss(jflo),a(iscr))

endif

*i acer.14997

c

subroutine alax(nin,nlax,fluor,a)

c     ******************************************************************

c     generate fluorescence data in the cashwell-everett format.

c     ******************************************************************

implicit real*8 (a-h,o-z)

common/util/npage,iverf

common/cont/c1h,c2h,l1h,l2h,n1h,n2h,math,mfh,mth,nsh,nsp,nsc

common/mainio/nsysi,nsyso,nsyse,ntty

common/ace1/tempd,err,matd,nbina,nbinp,negn,iprint,iopt,ndigit

dimension fluor(*)

dimension a(*)

dimension loc(50)

dimension enl(3),rhol(3),wtl(3)

*if sw

data dn/.9999d0/

data up/1.0001d0/

data emev/1.d6/

*else

data dn/.9999e0/

data up/1.0001e0/

data emev/1.e6/

*endif

c

c     ***charge for desired material

iz=matd/100

c

c     ***read in the atomic relaxation file for the desired material

call openz(nlax,0)

call tpidio(nlax,0,0,a,nw,nb)

110 call contio(nlax,0,0,a,nw,nb)

if (math.gt.0) go to 120

call error('alax','mat not found',' ')

120 if (math.eq.matd) go to 130

call tomend(nlax,0,0,a)

go to 110

130 call tofend(nlax,0,0,a)

call contio(nlax,0,0,a,nw,nb)

nss=n1h

ll=1

do iss=1,nss

loc(iss)=ll

call listio(nlax,0,0,a(ll),nb,nw)

ntr=n2h

ll=ll+nw

do while (nb.ne.0)

call moreio(nlax,0,0,a(ll),nb,nw)

ll=ll+nw

enddo

enddo

c

c     ***read in the photoionization cross section for the material

kk=ll

call openz(nin,0)

call tpidio(nin,0,0,a(ll),nw,b)

210 call contio(nin,0,0,a(ll),nw,b)

if (math.gt.0) go to 220

call error('spect','mat not found',' ')

220 if (math.eq.matd) go to 230

call tomend(nin,0,0,a(ll))

go to 210

230 call tofend(nin,0,0,a(ll))

call findf(matd,23,522,nin)

call contio(nin,0,0,a(ll),nw,nb)

e=0

call gety1(e,en,idis,sig,nin,a(ll))

c

c     ***for z>30, get the l1, l2, and l3 edges and jumps

if (iz.gt.30) then

do i=1,3

jj=loc(5-i)

enl(4-i)=a(jj+6)

e=dn*enl(4-i)

call gety1(e,en,idis,slo,nin,a(ll))

e=up*enl(4-i)

call gety1(e,en,idis,shi,nin,a(ll))

rhol(4-i)=slo/shi

enddo

endif

c

c     ***get the energy and jump of the k edge

ek=a(7)

e=dn*ek

call gety1(e,en,idis,slo,nin,a(ll))

e=up*ek

call gety1(e,en,idis,shi,nin,a(ll))

rhok=slo/shi

c

c     ***case of 11<z<20

if (iz.gt.11.and.iz.lt.20) then

c

c        ***average all the transitions to the k shell

n=nint(a(6))

sum1=0

sum2=0

do i=1,n

jj=8+6*i

if (nint(a(jj)).eq.0) then

sum1=sum1+a(jj+2)

sum2=sum2+a(jj+1)*a(jj+2)

endif

enddo

sum2=sum2/sum1

c

c        ***store the results

fluor(1)=ek/emev

fluor(2)=ek/emev

fluor(3)=rhok

fluor(4)=1

fluor(5)=0

fluor(6)=(1-rhok)*sum1

fluor(7)=0

fluor(8)=sum2/emev

c

c     ***case of z>19 and z<31

else if (iz.gt.19.and.iz.lt.31) then

c

c        ***extract l2, l3, and total for higher shells

n=nint(a(6))

sum1=0

sum2=0

do i=1,n

jj=8+6*i

if (nint(a(jj)).eq.0.and.nint(a(jj-1)).eq.3) then

el2=a(jj+1)

pl2=a(jj+2)

else if (nint(a(jj)).eq.0.and.nint(a(jj-1)).eq.4) then

el3=a(jj+1)

pl3=a(jj+2)

else if (nint(a(jj)).eq.0.and.nint(a(jj-1)).gt.4) then

sum1=sum1+a(jj+2)

sum2=sum2+a(jj+1)*a(jj+2)

endif

enddo

sum2=sum2/sum1

c

c        ***store the results

tot=(pl2+pl3+sum1)/(1-rhok)

y=0

phi=rhok

fluor(1)=ek/emev

fluor(5)=phi

fluor(9)=y

fluor(13)=0

phi=phi+pl3/tot

y=y+(1-rhok)*pl3

fluor(2)=ek/emev

fluor(6)=phi

fluor(10)=y

fluor(14)=el3/emev

phi=phi+pl2/tot

y=y+(1-rhok)*pl2

fluor(3)=ek/emev

fluor(7)=phi

fluor(11)=y

fluor(15)=el2/emev

phi=1

y=y+(1-rhok)*sum1

fluor(4)=ek/emev

fluor(8)=phi

fluor(12)=y

fluor(16)=sum2/emev

c

c     ***all other z values

else

rholt=rhol(1)*rhol(2)*rhol(3)

elav=(enl(1)+enl(2)+enl(3))/3

wtl(1)=1/rhol(1)

wtl(2)=wtl(1)/rhol(2)

wtl(3)=wtl(2)/rhol(3)

denom=wtl(3)-1

wtl(3)=(wtl(3)-wtl(2))/denom

wtl(2)=(wtl(2)-wtl(1))/denom

wtl(1)=(wtl(1)-1)/denom

c

c        ***compute the average yield and energy for l fluorescence

sum1=0

sum2=0

do iss=2,4

jj=loc(iss)

n=nint(a(jj+5))

wt=wtl(iss-1)

do i=1,n

if (nint(a(jj+7+6*i)).eq.0) then

sum1=sum1+a(jj+9+6*i)*wt

sum2=sum2+a(jj+8+6*i)*a(jj+9+6*i)*wt

endif

enddo

enddo

sum2=sum2/sum1

ylt=sum1

flt=sum2

if (flt.gt.enl(1)) then

write(nsyso,'('' L edge problem'')')

write(nsyso,'(1x,3f10.4)') flt,enl(1),elav

endif

c

c        ***extract kalpha1, kalpha2, kbeta1, and kbeta2

n=nint(a(6))

sum11=0

sum12=0

sum21=0

sum22=0

do i=1,n

jj=8+6*i

if (nint(a(jj)).eq.0) then

mm=nint(a(jj-1))

if (mm.eq.3) then

el2=a(jj+1)

pl2=a(jj+2)

else if (mm.eq.4) then

el3=a(jj+1)

pl3=a(jj+2)

else if (mm.ge.5.and.mm.le.9) then

sum11=sum11+a(jj+2)

sum12=sum12+a(jj+1)*a(jj+2)

else if (mm.ge.10.and.mm.le.16) then

sum21=sum21+a(jj+2)

sum22=sum22+a(jj+1)*a(jj+2)

endif

endif

enddo

if (iz.ge.37) then

sum22=sum22/sum21

else

sum11=sum11+sum21

sum12=sum12+sum22

sum21=0

endif

sum12=sum12/sum11

c

c        ***store the results

n=5

if (iz.gt.36) n=6

fluor(1)=elav/emev

fluor(1+n)=rholt

fluor(1+2*n)=0

fluor(1+3*n)=0

y=(1-rholt)*ylt

fluor(2)=elav/emev

fluor(2+n)=1

fluor(2+2*n)=y

fluor(2+3*n)=flt/emev

phi=1/rhok

phik=phi-1

tot=(pl2+pl3+sum11+sum21)/phik

phi=1

phi=phi+pl3/tot

y=y+phik*pl3

fluor(3)=ek/emev

fluor(3+n)=phi

fluor(3+2*n)=y

fluor(3+3*n)=el3/emev

phi=phi+pl2/tot

y=y+phik*pl2

fluor(4)=ek/emev

fluor(4+n)=phi

fluor(4+2*n)=y

fluor(4+3*n)=el2/emev

phi=phi+sum11/tot

y=y+phik*sum11

fluor(5)=ek/emev

fluor(5+n)=phi

fluor(5+2*n)=y

fluor(5+3*n)=sum12/emev

if (iz.ge.37) then

phi=phi+sum21/tot

y=y+phik*sum21

fluor(6)=ek/emev

fluor(6+n)=phi

fluor(6+2*n)=y

fluor(6+3*n)=sum22/emev

endif

c

endif

return

end

*i acer.15088

c

c     ***print the fluorescence data

if (nflo.gt.0) then

write(nsyso,'(//

&     '' fluorescence data''/

&     '' -----------------'')')

write(nsyso,'(/

&     ''          edge       phi         y           f''/

&     ''    ----------   -------   -------   ---------'')')

do i=1,nflo

write(nsyso,'(3x,f11.7,f10.4,f10.4,2x,f10.6)')

&        (xss(jflo+i-1+nflo*(j-1)),j=1,4)

enddo

endif

*i acer.15147

c

c        ***fluorescence data block

l=jflo

if (nflo.ne.0) then

do i=1,4*nflo

call typen(l,nout,2)

l=l+1

enddo

endif

*ident up70

*/ acer -- 20feb02

*/  add consistency checks for delayed neutrons

*/  add plots for nubar and delayed neutron spectra

*d acer.17720

integer dndat,dnd,ptype,ploct,hpd,sigh,dlwh

*d acer.17723

common/nxst/len2,izaid,nes,ntr,nr,ntrp,ntyph,ndnf,nxsd(8)

*d acer.17726

&  iurpt,nud,dndat,ldnd,dnd,jxsd(2),ptype,ntro,ploct

*i acer.18202

c

c     ***check delayed neutron data

if (ndnf.gt.0) then

write(nsyso,'(/'' check delayed neutron fractions'')')

l=dndat

sum=0

do j=1,ndnf

l=l+2

nn=nint(xss(l))

l=l+nn

frac=xss(l+1)

sum=sum+frac

l=l+nn+1

enddo

if (abs(sum-1)*1000.gt.one) then

write(nsyso,'(''   consis: delayed fractions do not'',

&        '' sum to one'')')

nerr=nerr+1

endif

write(nsyso,'(/'' check delayed neutron distributions'')')

do i=1,ndnf

nlaw=1

loct=nint(xss(i-1+ldnd)+dnd-1)

law=nint(xss(loct+1))

m=nint(xss(loct+3))

loct=loct+3+2*m

loct=loct+1

n=nint(xss(loct))

loct=loct+1+2*n

m=nint(xss(loct))

loct=loct+2*m

loct=loct+1

ne=nint(xss(loct))

loci=nint(xss(1+ne+loct))+dnd-1

intt=nint(xss(loci))

n=nint(xss(loci+1))

loci=loci+1

do j=1,n

x=xss(j+loci)

y=xss(j+loci+n)

c=xss(j+loci+2*n)

if (j.gt.1) then

if (x.lt.xlast) then

write(nsyso,'(''   consis: delayed spectrum'',

&                 '' energies not monotonic'')')

nerr=nerr+1

endif

if (c.lt.clast) then

write(nsyso,'(''   consis: delayed spectrum'',

&                 '' cummulative probs not monotonic'')')

nerr=nerr+1

endif

endif

xlast=x

clast=c

enddo

enddo

endif

*d acer.18530

common/nxst/len2,izaid,nes,ntr,nr,ntrp,ntyph,ndnf,nxsd(8)

*i acer.19514

c

c     ***plot nubar

if (nu.gt.0) call aplonu(nout,iwcol)

*i acer.19517

c

c     ***plot delayed-neutron data

if (ndnf.gt.0) call aplodn(nout,iwcol)

*i acer.20148

c

subroutine aplonu(nout,iwcol)

c     ******************************************************************

c     plot the total fission nubar curve

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

integer esz,sig,and,tyr,dlw,gpd,fis,sigp,andp,dlwp,yp,end

common/nxst/len2,izaid,nes,ntr,nr,ntrp,ntype,nxsd(9)

common/jxst/esz,nu,mtr,lqr,tyr,lsig,sig,land,and,ldlw,dlw,

&  gpd,mtrp,lsigp,sigp,landp,andp,ldlwp,dlwp,yp,fis,end,jxsd(10)

character hz*13,hd*10,hk*70,hm*10

common/mis1/hz,hd,hk,hm

common/xsst/xss(3000000),n3

common/ace7/awi,izai,mcnpx,newfor

character*1 qu

character*10 name

data qu/''''/

*if sw

data big/1.d10/

data small/1.d-12/

data ten/10.d0/

data step/0.2d0/

*else

data big/1.e10/

data ten/10.e0/

data small/1.e-12/

data step/0.2e0/

*endif

zero=0

one=1

c

c     ***set up the page for the total nubar curve

xmin=big

xmax=0

ymin=big

ymax=-big

l=nu

j=nint(xss(l))

kf=j

if (kf.lt.0) then

l=l+iabs(kf)+1

j=nint(xss(l))

endif

if (j.ne.2) then

e=xss(esz)

emax=xss(esz+nes-1)

l=l+1

n=nint(xss(l))

ymin=xss(l+1)

ymax=ymin

do i=2,n

ymax=ymax+xss(l+i)*e**(i-1)

enddo

else

l=l+1

nr=nint(xss(l))

if (nr.gt.0) l=l+2*nr

l=l+1

ne=nint(xss(l))

do i=1,ne

x=xss(l+i)

y=xss(l+i+ne)

if (x.lt.xmin) xmin=x

if (x.gt.xmax) xmax=x

if (y.lt.ymin) ymin=y

if (y.gt.ymax) ymax=y

enddo

endif

call ascle(4,ymin,ymax,major,minor)

ystep=(ymax-ymin)/major

xstep=(xmax-xmin)/4

write(nout,'(''1'',i3,''/'')') iwcol

it=1

do i=1,70

if (hk(i:i).ne.' ') it=i

enddo

write(nout,'(a,''<'',a,''>'',a,''/'')') qu,hk(1:it),qu

write(nout,'(a,''<t>otal fission nubar'',a,''/'')') qu,qu

write(nout,'(''1 0 2/'')')

write(nout,'(1p,3e12.3,''/'')') xmin,xmax,xstep

write(nout,'(a,''<e>nergy (<m>e<v>)'',a,''/'')') qu,qu

write(nout,'(1p,3e12.3,''/'')') ymin,ymax,ystep

write(nout,'(a,''<f>ission nubar'',a,''/'')') qu,qu

write(nout,'(''/'')')

write(nout,'(''/'')')

write(nout,'(''0/'')')

l=nu

j=nint(xss(l))

kf=j

if (kf.lt.0) then

l=l+iabs(kf)+1

j=nint(xss(l))

endif

if (j.ne.2) then

e=xss(esz)

emax=xss(esz+nes-1)

l=l+1

n=nint(xss(l))

do while (e.lt.emax)

sum=xss(l+1)

do i=2,n

sum=sum+xss(l+i)*e**(i-1)

enddo

write(nout,'(1p,2e14.6,''/'')') e,sum

e=e+step

enddo

else

l=l+1

nr=nint(xss(l))

if (nr.gt.0) l=l+2*nr

l=l+1

ne=nint(xss(l))

do i=1,ne

x=xss(l+i)

y=xss(l+i+ne)

write(nout,'(1p,2e14.6,''/'')') x,y

enddo

endif

write(nout,'(''/'')')

return

end

*i acer.20593

c

subroutine aplodn(nout,iwcol)

c     ******************************************************************

c     plot the delayed-neutron data

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

integer esz,sig,and,tyr,dlw,gpd,fis,sigp,andp,dlwp,yp,end

integer dndat,dnd,ptype,ploct

common/nxst/len2,izaid,nes,ntr,nr,ntrp,ntype,ndnf,nxsd(8)

common/jxst/esz,nu,mtr,lqr,tyr,lsig,sig,land,and,ldlw,dlw,

&  gpd,mtrp,lsigp,sigp,landp,andp,ldlwp,dlwp,yp,fis,end,

&  iurpt,nud,dndat,ldnd,dnd,jxsd(2),ptype,ntro,ploct

character hz*13,hd*10,hk*70,hm*10

common/mis1/hz,hd,hk,hm

common/xsst/xss(3000000),n3

common/ace7/awi,izai,mcnpx,newfor

character*1 qu

character*10 name

external ascll,ascle

data qu/''''/

*if sw

data big/1.d10/

data small/1.d-12/

data ten/10.d0/

data step/1.2d0/

data scale/1.d2/

*else

data big/1.e10/

data ten/10.e0/

data small/1.e-12/

data step/1.2e0/

data scale/1.e2/

*endif

zero=0

one=1

c

c     ***set up the page for the delayed nubar curve

xmin=big

xmax=0

ymin=big

ymax=-big

l=nud

j=nint(xss(l))

l=l+1

nr=nint(xss(l))

if (nr.gt.0) l=l+2*nr

l=l+1

ne=nint(xss(l))

do i=1,ne

x=xss(l+i)

y=xss(l+i+ne)

if (x.lt.xmin) xmin=x

if (x.gt.xmax) xmax=x

if (y.lt.ymin) ymin=y

if (y.gt.ymax) ymax=y

enddo

ymin=ymin/step

ymax=ymax*step

call ascle(4,ymin,ymax,major,minor)

ystep=(ymax-ymin)/major

xstep=(xmax-xmin)/4

write(nout,'(''1'',i3,''/'')') iwcol

it=1

do i=1,70

if (hk(i:i).ne.' ') it=i

enddo

write(nout,'(a,''<'',a,''>'',a,''/'')') qu,hk(1:it),qu

write(nout,'(a,''<d>elayed nubar'',a,''/'')') qu,qu

write(nout,'(''1 0 2/'')')

write(nout,'(1p,3e12.3,''/'')') xmin,xmax,xstep

write(nout,'(a,''<e>nergy (<m>e<v>)'',a,''/'')') qu,qu

write(nout,'(1p,3e12.3,''/'')') ymin,ymax,ystep

write(nout,'(a,''<d>elayed nubar'',a,''/'')') qu,qu

write(nout,'(''/'')')

write(nout,'(''/'')')

write(nout,'(''0/'')')

l=nud

j=nint(xss(l))

l=l+1

nr=nint(xss(l))

if (nr.gt.0) l=l+2*nr

l=l+1

ne=nint(xss(l))

do i=1,ne

x=xss(l+i)

y=xss(l+i+ne)

write(nout,'(1p,2e14.6,''/'')') x,y

enddo

write(nout,'(''/'')')

c

c     ***set up the page for the delayed spectra curves

xmin=big

xmax=0

ymin=big

ymax=-big

do i=1,ndnf

nlaw=1

loct=nint(xss(i-1+ldnd)+dnd-1)

law=nint(xss(loct+1))

m=nint(xss(loct+3))

loct=loct+3+2*m

loct=loct+1

n=nint(xss(loct))

loct=loct+1+2*n

m=nint(xss(loct))

loct=loct+2*m

loct=loct+1

ne=nint(xss(loct))

loci=nint(xss(1+ne+loct))+dnd-1

intt=nint(xss(loci))

n=nint(xss(loci+1))

loci=loci+1

l=dndat

do j=1,ndnf

if (j.eq.i) decay=xss(l)

l=l+2

nn=nint(xss(l))

l=l+nn

if (j.eq.i) frac=xss(l+1)

l=l+nn+1

enddo

do j=1,n

x=xss(j+loci)

if (x.eq.zero) x=xss(j+1+loci)/10

y=frac*xss(j+loci+n)

if (x.lt.xmin) xmin=x

if (x.gt.xmax) xmax=x

if (y.lt.ymin) ymin=y

if (y.gt.ymax) ymax=y

enddo

enddo

call ascll(xmin,xmax)

if (ymin.lt.ymax/scale) ymin=ymax/scale

call ascll(ymin,ymax)

write(nout,'(''1'',i3,''/'')') iwcol

it=1

do i=1,70

if (hk(i:i).ne.' ') it=i

enddo

write(nout,'(a,''<'',a,''>'',a,''/'')') qu,hk(1:it),qu

write(nout,'(a,''<d>elayed neutron spectra'',a,''/'')') qu,qu

xtag=step*xmin

ytag=ymax/30

write(nout,'(''4 0 2 1'',2e12.4,''/'')') xtag,ytag

write(nout,'(1p,3e12.3,''/'')') xmin,xmax,one

write(nout,'(a,''<e>nergy (<m>e<v>)'',a,''/'')') qu,qu

write(nout,'(1p,3e12.3,''/'')') ymin,ymax,one

write(nout,'(a,''<p>robability'',a,''/'')') qu,qu

write(nout,'(''/'')')

do i=1,ndnf

if (i.gt.1) then

write(nout,'(i2,''/'')') i

write(nout,'(''/'')')

endif

if (iwcol.eq.0) then

write(nout,'(''0 0'',i2,''/'')') i

else

write(nout,'(''0 0 0'',i2,''/'')') i

endif

l=dndat

do j=1,ndnf

if (j.eq.i) decay=xss(l)

l=l+2

n=nint(xss(l))

l=l+n

if (j.eq.i) frac=xss(l+1)

l=l+n+1

enddo

write(nout,'(a,''group'',i2,'' frac'',f7.4,'' decay/shake'',

&     1p,e10.3,a,''/'')') qu,i,frac,decay,qu

write(nout,'(''0/'')')

loct=nint(xss(i-1+ldnd)+dnd-1)

law=nint(xss(loct+1))

m=nint(xss(loct+3))

loct=loct+3+2*m

loct=loct+1

n=nint(xss(loct))

loct=loct+1+2*n

m=nint(xss(loct))

loct=loct+2*m

loct=loct+1

ne=nint(xss(loct))

loci=nint(xss(1+ne+loct))+dnd-1

intt=nint(xss(loci))

n=nint(xss(loci+1))

loci=loci+1

m=n

if (intt.eq.1) m=m-1

do j=1,m

x=xss(j+loci)

if (x.eq.zero) x=xss(j+1+loci)/10

y=frac*xss(j+loci+n)

if (y.lt.ymin) y=ymin

write(nout,'(1p,2e14.6,''/'')') x,y

if (intt.eq.1) then

x=xss(j+1+loci)

y=frac*xss(j+loci+n)

if (y.lt.ymin) y=ymin

write(nout,'(1p,2e14.6,''/'')') x,y

endif

enddo

write(nout,'(''/'')')

enddo

return

end

*ident up71

*/ reconr -- 25aug02

*/  if the cross section or yield in a section is zero at all

*/  energies, the union grid is spoiled.  we fix lunion so the

*/  so called pseudo-threshold search cannot go past one less

*/  than the number of points in the section.  this problem was

*/  seen in n-15 of jendl-3.3 for 12/104 and 12/105.

*i reconr.1742

npr=nint(a(iscr+5))

*d reconr.1764

if (sr.lt.ssmall.and.srnext.lt.ssmall.and.ir.lt.npr-1) go to 205

*ident up72

*/ acer -- 3sep02

*/  watch for a special case in plotting

*d acer.21528

*d up59.8

i1=1

if (ne.gt.2) then

i1=2

if (ymax.gt.test*xss(l3+2+ne-2)) ymax=xss(l3+2+ne-2)

endif

do ie=i1,ne

*ident up73

*/ groupr -- 3sep02

*/  allow for up to 8 groups of delayed neutrons as used in some

*/  materials of jeff-3.

*d groupr.240

common/delayg/ndelg

common/delayn/dntc(8)

*d groupr.567

do i=1,ndelg

*d groupr.570,571

nll=ndelg

l=ians+ndelg

*i groupr.3071

common/delayg/ndelg

*d groupr.3100

if (mfd.eq.5.and.mtd.eq.455) nl=ndelg

*d groupr.3391

common/delayn/dntc(8)

*d groupr.3802

common/delayn/dntc(8)

*d groupr.3842

if (lnd.gt.8) call error('getyld','illegal lnd.',' ')

*i groupr.4272

common/delayg/ndelg

*d groupr.4386

if (mtd.eq.455) nk=ndelg

*i groupr.7934

common/delayg/ndelg

*i groupr.7955

ndelg=0

*i groupr.8380

if (mth.eq.455) then

call listio(nin,nout,nscr,a(iscr),nb,nw)

ndelg=n1h

endif

*ident up74

*/ groupr -- 03sep02

*/  fix editing error in the lwr epri weight function.

*/  reported by skip kahler (bechtel bettis).

*d groupr.2171

& 1.407d7,1.154d-6,1.42d7,1.087d-6,1.43d7,9.5757d-7,1.44d7,

*d groupr.2234

& 1.407e7,1.154e-6,1.42e7,1.087e-6,1.43e7,9.5757e-7,1.44e7,

*/  fix an incorrect boolean statement in the removal of upscatter

*/  in subroutine getsed.  reported by kazuaki (sae, japan).

*d groupr.8914

if (mtd.lt.18.or.(mtd.gt.21.and.mtd.ne.38)) then

*ident up75

*/ acer -- 09oct02

*/  fix some typographical errors in recent updates

*d up69.82,83

call tpidio(nlax,0,0,a,nb,nw)

110 call contio(nlax,0,0,a,nb,nw)

*d up69.90

call contio(nlax,0,0,a,nb,nw)

*d up69.107,108

call tpidio(nin,0,0,a(ll),nb,nw)

210 call contio(nin,0,0,a(ll),nb,nw)

*d up69.116

call contio(nin,0,0,a(ll),nb,nw)

*ident up76

*/ plotr -- 09oct02

*/  allow for more energy resolutions in plotr output

*/  for looking at the details of resonance reconstruction

*d plotr.1939

write(nplt,'(1p,2e16.8,''/'')') x(i),y(i)

*d plotr.1941,1942

write(nplt,'(1p,6e16.8,''/'')') x(i),y(i),

&        dym(i),dyp(i),dxm(i),dxp(i)

*ident up77

*/ plotr -- 11oct02

*/  add a capability to plot percent difference or ratios

*i plotr.21

c     * percent difference and ratio plots can be requested.           *

*d plotr.178

c     *            ntp   special features                              *

c     *                  1 for regular plots (default)                 *

c     *                  2 for percent difference plots                *

c     *                     read a second "card 8" for percent diff    *

c     *                     of second curve with respect to first      *

c     *                  3 for ratio plots                             *

c     *                     read a second "card 8" for ratio           *

c     *                     of second curve to first                   *

*i plotr.630

if (mfd.eq.3.and.ntp.gt.1) then

nin2=0

matd2=0

matd2=0

mtd2=0

temper2=0

nth2=1

ntp2=1

nkh2=1

read(nsysi,*)

&        iverf2,nin2,matd2,mfd2,mtd2,temper2,nth2,ntp2,nkh2

call openz(nin2,0)

write(nsyso,'(/

&        '' iverf2 ............................... '',i10/

&        '' nin2 ................................. '',i10/

&        '' matd2 ................................ '',i10/

&        '' mfd2 ................................. '',i10/

&        '' mtd2 ................................. '',i10/

&        '' temp2 ................................ '',1p,e10.2/

&        '' nth2 ................................. '',i10/

&        '' ntp2 ................................. '',i10/

&        '' nkh2 ................................. '',i10)')

&        iverf2,nin2,matd2,mfd2,mtd2,temper2,nth2,ntp2,nkh2

endif

*i plotr.702

if (nin2.ne.0) call tpidio(nin2,0,0,a,nb,nw)

*i plotr.726

if (nin2.eq.0) go to 320

idone=0

do while (idone.eq.0)

call contio(nin2,0,0,a,nb,nw)

if (math.lt.0) then

write(strng,

&        '(''desired mat2 and temp2 not found '',i4,f10.1)')

&         matd2,temper2

call error('plotr',strng,' ')

endif

if (math.eq.matd2) then

if (mfd2.eq.7) then

idone=1

else

if (iverf2.ge.5) call contio(nin2,0,0,a,nb,nw)

if (iverf2.ge.6) call contio(nin2,0,0,a,nb,nw)

call contio(nin2,0,0,a,nb,nw)

tem=a(1)

if (abs(tem-temper2).le.temper2/1000) idone=1

endif

endif

if (idone.eq.0) call tomend(nin2,0,0,a)

enddo

*i plotr.729

if (nin2.ne.0) call findf(matd2,mfd2,mtd2,nin2)

*i plotr.730

if (nin2.ne.0) call contio(nin2,0,0,a,nb,nw)

*i plotr.990

else if (nin2.ne.0) then

enext=big

reset=-1

loc2=50+npage

call getz(reset,enxt,idis,zz,0,a)

call getz(enow,enxt,idis,zz,nin,a)

if (enxt.lt.enext) enext=enxt

call getz(enow,enxt,idis,zz,nin2,a(loc2))

if (enxt.lt.enext) enext=enxt

*i plotr.1072

else if (nin2.ne.0) then

enext=big

call getz(enow,enxt,idis,zz,nin,a)

if (enxt.lt.enext) enext=enxt

call getz(enow,enxt,idis,z2,nin2,a(loc2))

if (enxt.lt.enext) enext=enxt

if (ntp.eq.2) then

yf=100*(z2-zz)

if (zz.ne.zero) yf=yf/zz

else if (ntp.eq.3) then

yf=z2

if (zz.ne.zero) yf=yf/zz

endif

*i plotr.1102

else if (nin2.ne.0) then

enext=big

call getz(enow,enxt,idis,zz,nin,a)

if (enxt.lt.enext) enext=enxt

call getz(enow,enxt,idis,z2,nin2,a(loc2))

if (enxt.lt.enext) enext=enxt

if (ntp.eq.2) then

yf=100*(z2-zz)

if (zz.ne.zero) yf=yf/zz

else if (ntp.eq.3) then

yf=z2

if (zz.ne.zero) yf=yf/zz

endif

*i plotr.2104

c

subroutine getz(x,xnext,idis,z,itape,a)

c     ******************************************************************

c     retrieve z(x) from an endf/b tab1 structure using paged bcd or

c     blocked binary formats.  call with x=0 to read in first page

c     or block of data and initialize pointers.  routine assumes

c     values will be called in ascending order.  xnext is the first

c     data grid point greater than x unless x is the last point.

c     this version will keep track of pointers for up to 10 units.

c     call with x=-1 to clear the pointers before each group of files.

c     based on gety from mixr.

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

dimension a(*)

common/getzc/ntape,jtape(10),nrt(10),npt(10),irt(10),ipt(10),

&  ip1t(10),ip2t(10),nbt(10),nwt(10)

save lt

external tab1io,error,moreio,terp1

*if sw

data big/1.d10/

*else

data big/1.e10/

*endif

zero=0

c

c     ***branch on value of x

idis=0

if (x.eq.zero) go to 100

if (x.gt.zero) go to 115

c

c     ***clear pointer storage

ntape=0

return

c

c     ***read first page or block of data and initialize

100 ntape=ntape+1

jtape(ntape)=itape

call tab1io(itape,0,0,a,nb,nw)

nwtot=nw

nr=nint(a(5))

np=nint(a(6))

lt=6+2*nr

ip1=1

ip2=(nw-lt)/2

if (nb.eq.0) ip2=ip2+2

ir=1

ip=2

xnext=a(lt+1)

c

c     ***save pointers and return

nrt(ntape)=nr

npt(ntape)=np

irt(ntape)=ir

ipt(ntape)=ip

ip1t(ntape)=ip1

ip2t(ntape)=ip2

nbt(ntape)=nb

nwt(ntape)=nwtot

return

c

c     ***restore pointers

115 if (ntape.eq.0)

&  call error('gety','not properly initialized',' ')

do 120 i=1,ntape

if (jtape(i).ne.itape) go to 120

ktape=i

nr=nrt(i)

np=npt(i)

ir=irt(i)

ip=ipt(i)

ip1=ip1t(i)

ip2=ip2t(i)

nb=nbt(i)

nwtot=nwt(i)

go to 125

120 continue

z=0

xnext=big

return

c

c     ***is x in this panel

125 ln=2*(ip-ip1)+lt

if (x.lt.a(ln-1)) go to 135

if (x.lt.a(ln+1)) go to 130

if (ip.eq.np) go to 140

c

c     ***no.  move up to next range.

c     ***read in new page of data if needed.

ip=ip+1

nbx=nint(a(5+2*ir))

if (ip.gt.nbx) ir=ir+1

if (ip.lt.ip2) go to 125

if (nb.eq.0) go to 130

a(lt+1)=a(nwtot-3)

a(lt+2)=a(nwtot-2)

a(lt+3)=a(nwtot-1)

a(lt+4)=a(nwtot)

call moreio(itape,0,0,a(lt+5),nb,nw)

nwtot=nw+lt+4

ip1=ip-1

ip2=ip1+nw/2+1

if (nb.eq.0) ip2=ip2+2

go to 125

c

c     ***yes.  interpolate for desired value

130 int=nint(a(6+2*ir))

if (int.eq.1) idis=1

call terp1(a(ln-1),a(ln),a(ln+1),a(ln+2),x,z,int)

xnext=a(ln+1)

if ((ln+3).gt.nwtot.and.nb.eq.0) return

xn=a(ln+3)

if (xn.eq.xnext) idis=1

go to 150

c

c     ***special branch for x outside range of table

135 z=0

xnext=a(ln-1)

go to 150

c

c     ***special branch for last point

140 z=a(ln+2)

xnext=big

c

c     ***save pointers and return

150 nrt(ktape)=nr

npt(ktape)=np

irt(ktape)=ir

ipt(ktape)=ip

ip1t(ktape)=ip1

ip2t(ktape)=ip2

nbt(ktape)=nb

nwt(ktape)=nwtot

return

end

*ident up78

*/ broadr -- 10oct02

*/  tighten up the tolerances for integral thinning a bit

*d broadr.56

c     *             (errmax.ge.errthn, default=10*errthn)              *

*d broadr.58

c     *             (usage as in reconr) (default=errthn/20000)        *

*d broadr.177,178

if (errmax.eq.zero) errmax=10*errthn

if (errint.eq.zero) errint=errthn/20000

*/ broadr -- 10oct02

*/  fix some problems related to keeping computed cross sections

*/  on printable 7- or 9-digit grids.  this was discovered when

*/  doing testing at 0.01% for u235 above 1 kev, and it doesn't

*/  usually make itself evident for easier cases.

*i broadr.1080

xt=sqrt(alpha*es(2))

*d broadr.1087

call bsigma(k,xt,ss(1,2),e,s,nx)

*d broadr.1120

xt=sqrt(alpha*es(1))

call bsigma(k,xt,ss(1,1),e,s,nx)

*ident up79

*/ reconr -- 10oct02

*/  tighten up the default tolerances for integral thinning a bit

*d reconr.63

c     *             (errmax.ge.err, default=10*err)                    *

*d reconr.65

c     *             per grid point (default=err/20000)                 *

*d reconr.314

if (errmax.le.zero) errmax=10*err

*d reconr.316

if (errint.le.zero) errint=err/20000

*/ reconr -- 10oct02

*/  make some improvements in grid generation to make sure that

*/  all cross sections are computed on printable 7- or 9-digit

*/  energies and that the original nodes for resonance reconstruction

*/  are reasonable.  these changes were made to remove some small

*/  artifacts on the order of 0.05% above 1 kev for some materials.

*i reconr.341

do i=1,ngrid

a(ienode+i-1)=sigfig(a(ienode+i-1),7,0)

enddo

*d reconr.801

*d reconr.804

&         hw=hw+(a(jnow+3)+abs(a(jnow+4))+abs(a(jnow+5)))/2

ndig=5

if (a(jnow).gt.zero) ndig=2+nint(log10(a(jnow)/(hw/10)))

if (ndig.lt.5) ndig=5

if (ndig.gt.9) ndig=9

a(ienode+nodes-1)=sigfig(a(jnow),ndig,0)

*d reconr.810

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*d reconr.817

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*d reconr.900,901

hw=a(nloc+ien*jen+1)

ndig=5

if (ener.gt.zero) ndig=2+nint(log10(ener/(hw/10)))

if (ndig.lt.5) ndig=5

if (ndig.gt.9) ndig=9

a(ienode+nodes-1)=sigfig(ener,ndig,0)

*d reconr.907

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*d reconr.914

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*i reconr.993

ndig=5

if (enow.gt.zero) ndig=2+nint(log10(enow/(hw/10)))

if (ndig.lt.5) ndig=5

if (ndig.gt.9) ndig=9

*d reconr.998

a(ienode+nodes-1)=sigfig(enow,ndig,0)

*d reconr.1002

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*d reconr.1007

a(ienode+nodes-1)=sigfig(ehalf,ndig,0)

*d reconr.1103

a(ienode+nodes-1)=sigfig(ener,7,0)

*d reconr.1107

a(ieunr+nunr-1)=sigfig(ener,7,0)

*d reconr.1176

a(ienode+nodes-1)=sigfig(ener,7,0)

*d reconr.1180

a(ieunr+nunr-1)=sigfig(ener,7,0)

*d reconr.1194

a(ienode+nodes-1)=sigfig(ener,7,0)

*d reconr.1198

a(ieunr+nunr-1)=sigfig(ener,7,0)

*d reconr.1303

a(ienode+nodes-1)=sigfig(ener,7,0)

*d reconr.1307

a(ieunr+nunr-1)=sigfig(ener,7,0)

*d reconr.1322

a(ienode+nodes-1)=sigfig(ener,7,0)

*d reconr.1326

a(ieunr+nunr-1)=sigfig(ener,7,0)

*/  the printout for errors caused by significant figure reduction

*/  are obsolete now that we can go to 9 digits when necessary.

*/  we remove them and add a column for the error introduced into

*/  the fission integral by integral thinning.

*d reconr.2044

*d reconr.2046

*d reconr.2050

*i reconr.2051

fint=0

fmax=0

*d reconr.2074,2078

&  15x,''resonance integral check (errmax,errint)''//

&  4x,''upper'',6x,''elastic'',3x,''percent'',3x,

&  ''capture'',3x,''percent'',3x,''fission'',3x,''percent''/

&  4x,''energy'',5x,''integral'',3x,''error'',4x,

&  ''integral'',3x,''error'',4x,''integral'',3x,''error''/

&  1p,e10.2)') elo

*d reconr.2113,2139

*i reconr.2177

fmax=fmax+dm2*dx/(2*xm)

*i reconr.2202

c1=a(isigs+3*(i-1)+1)

c2=a(isigs+3*(i-2)+1)

fint=fint+(c1+c2)*dx/(2*xm)

*d reconr.2207,2214

if (cint.ne.zero) cmax=100*cmax/cint

if (eint.ne.zero) emax=100*emax/eint

if (fint.ne.zero) fmax=100*fmax/fint

write(nsyso,'(1p,e10.2,1x,3(1p,e12.2,f8.3))')

&  a(ix+i-2),eint,emax,cint,cmax,fint,fmax

*i reconr.2229

fint=0

*d reconr.2232,2233

fmax=0

*d reconr.2286

*d reconr.2288

&  ngneg,nmax,nrtot

*ident up80

*/ acer -- 10dec02

*/   fix the photoatomic energy grid to include the discontinuities

*/   at the photo edges.  reported by morgan white (lanl x-5).

*d acer.14736

e=sigfig(enext,7,0)

if (idis.ne.0) then

e=sigfig(e,7,-1)

call gety1(e,enxt,idis,s,nin,a(iscr))

l=l+1

xss(l)=e

e=sigfig(e,7,+2)

endif

*/  fix the values of the production cross section and heating

*/  at the particle production thresholds.

*i acer.8264

if (y.lt.delt) y=0

*i acer.9533

if (xss(hpd+2+naa+ie-it).lt.delt) xss(hpd+2+naa+ie-it)=0

*/  modify the acer listing to allow 6-digit energy indexes with

*/  the first column always blank.  this allows for materials with

*/  more than 99999 energy points.

*d acer.9863

&        '(''1''/6x,''i'',5x,''energy'',11x,'' total  '',7x,

*d acer.9865

&        ''gamma prod''/1x,''------'',3x,''--------------'',

*d acer.9868

&        '(''1''/6x,''i'',5x,''energy'',11x,'' total  '',7x,

*d acer.9870

&        1x,''------'',3x,''--------------'',

*d acer.9874

write(nsyso,'(1x,i6,1p,e17.8,7e15.6)') i,xss(esz+i),

*d acer.9877

write(nsyso,'(1x,i6,1p,e17.8,7e15.6)') i,xss(esz+i),

*d acer.9916

write(nsyso,'(''1''/6x,''i'',5x,''energy'',11x,a10,

*d acer.9918

write(nsyso,'(1x,''------'',3x,''--------------'',

*d acer.9929

write(nsyso,'(1x,i6,1p,e17.8,7a15)')

*/  the global value of ntr is being overwritten when charged particle

*/  production is present.  allow both fission flags.  this only

*/  affects the plots.  it showed up when processing a high-energy

*/  u-238 case with proton production by causing a bad plot of capture

*/  and fission resonance contours.

*d acer.12592

ntrh=nint(xss(ntro-1+i))

*d acer.12595

do k=1,ntrh

*d acer.12601

do k=1,ntrh

*d acer.12607

do k=1,ntrh

*d acer.12613

do j=1,ntrh

*d acer.12632

do k=1,ntrh

*d acer.12638

do ir=1,ntrh

*d acer.12682

do k=1,ntrh

*d acer.12688

do ii=1,ntrh

*d acer.18808

if (mt.eq.18.or.mt.eq.19) then

*ident up81

*/ moder -- 2dec02

*/   fix up the processing of the covariance sections to match

*/   the endf-6 format specifications.

*d moder.1282,1290

ner=n1h

do j=1,ner

call contio(nin,nout,nscr,a,nb,nw)

lru=l1h

nro=n1h

if (nro.gt.0) then

call contio(nin,nout,nscr,a,nb,nw)

ni=n2h

do k=1,ni

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

enddo

endif

call contio(nin,nout,nscr,a,nb,nw)

lcomp=l2h

nls=n1h

if (lru.eq.2) then

do l=1,nls

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

enddo

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

else if (lcomp.eq.0) then

do l=1,nls

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

enddo

else

call contio(nin,nout,nscr,a,nb,nw)

nsrs=n1h

nlrs=n2h

do k=1,nsrs

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

enddo

if (nlrs.gt.0) then

do k=1,nsrs

call listio(nin,nout,nscr,a,nb,nw)

do while (nb.ne.0)

call moreio(nin,nout,nscr,a,nb,nw)

enddo

enddo

endif

endif

enddo

*ident up82

*/ acer -- 28jan03

*/  the heating value in the photoatomic ace file is supposed to be

*/  used in an "f6" tally with the computed photon flux to compute

*/  the energy deposition from electrons, positrons, and atomic

*/  recoils.  the original heating value was designed to be used

*/  with an explicit calculation of heating during a coupled

*/  electron-photon calculation, and it only included the atomic

*/  recoil.  this update adds in the other parts of the heating.

*/  it was also necessary to modify the quadrature in iheat to

*/  handle the very high incident energies now given in endf.

*i up69.23

data epair/1.022d0/

*i up69.25

data epair/1.022e0/

*d acer.14745

eszg=1

*d acer.14767

e=xss(eszg-1+i)

*d acer.14769

xss(l-1+i)=s

*d acer.14838

call iheat(xss(i)*emev,en,idis,a(iscr),heat,siginc)

*d up61.20

xss(lhnm-1+i)=xss(iinc-1+i)*heat/emev

*d acer.14778

xss(eszg-1+i)=xss(eszg-1+i)/emev

*d acer.14780

*d acer.14783

jinc=next

*i acer.14844

do i=1,nes

xss(lhnm-1+i)=xss(lhnm-1+i)+xss(eszg-1+i)*xss(iabs-1+i)

enddo

*d up69.50

call alax(nin,nlax,xss(jflo),xss(eszg),xss(iabs),xss(lhnm),

1     a(iscr),nes)

*i up69.51

c

c     ***add in heating contribution from pair production

do i=1,nes

xss(lhnm-1+i)=xss(lhnm-1+i)

1     +xss(ipair-1+i)*(xss(eszg-1+i)-epair)

enddo

c

c     ***convert heating to a per collision basis

do i=1,nes

tot=xss(iinc-1+i)+xss(icoh-1+i)+xss(iabs-1+i)+xss(ipair-1+i)

xss(lhnm-1+i)=xss(lhnm-1+i)/tot

enddo

*i acer.14934

c     ***also limit panels by the fractional energy change.

*i acer.14956

if (pnext.lt.pnow/2) pnext=pnow/2

*d acer.14993

heat=e-ebar

*d up69.54

subroutine alax(nin,nlax,fluor,ener,abs,heat,a,nes)

*i up69.63

dimension ener(nes),abs(nes),heat(nes)

*i up69.155

c

c        ***subtract the photon energy from the heating

do i=1,nes

if (ener(i).gt.ek/emev) heat(i)=heat(i)

1        -abs(i)*sum1*sum2/emev

enddo

*i up69.187

c

c        ***subtract the photon energy from the heating

do i=1,nes

if (ener(i).gt.ek/emev) heat(i)=heat(i)-abs(i)

1        *(sum1*sum2+el2*pl2+el3*pl3)/emev

enddo

*i up69.282

c

c        ***subtract the photon energy from the heating

do i=1,nes

if (ener(i).gt.elav/emev) heat(i)=heat(i)

1        -abs(i)*ylt*flt/emev

if (ener(i).gt.ek/emev) heat(i)=heat(i)

1        -abs(i)*(sum11*sum12+sum21*sum22

2        +el2*pl2+el3*pl3)/emev

enddo

*ident up83

*/ plotr -- 12feb03

*/  fixes an error in plotr that prevents it from printing out

*/  negative values of percent differences.  zero percent

*/  difference confuses the thinning logic, so we add a small

*/  amount to all the percent differences.

*d up77.88

yf=100*(z2-zz)+small

*d up77.102

yf=100*(z2-zz)+small

*d plotr.1113,1114

if (itype.eq.1) then

if (yf.eq.zero.and.y(n).gt.zero) go to 380

if (yf.gt.zero.and.y(n).eq.zero) go to 380

else

test=ten**(-15)

if (yf.le.test) yf=test

if (yf.eq.test.and.y(n).gt.test) go to 380

if (yf.gt.test.and.y(n).eq.test) go to 380

endif

*d plotr.1118,1122

375 if (idis.gt.0) go to 380

if (itype.eq.3) then

if (yf.eq.zero.and.y(n).gt.zero) go to 380

if (yf.gt.zero.and.y(n).eq.zero) go to 380

else

test=ten**(-15)

if (yf.le.test) yf=test

if (yf.eq.test.and.y(n).gt.test) go to 380

if (yf.gt.test.and.y(n).eq.test) go to 380

endif

*d plotr.1136

if (yf.ne.zero.and.itype.ne.2.and.itype.ne.4) nlast=n

*ident up84

*/ purr -- 30sep02

*/  change the sampling scheme to use a different set of total cross

*/  section bins for each temperature.  change the binning logic to

*/  use approximately equally probable bins over most of the range

*/  with two bins of lower probabilities on the low and high ends.

*d purr.56

common/pustore/a(160000)

*d purr.72

data namax/160000/, nidmax/24/, ipr/1/

*d purr.78

nsamp=5000

*d purr.136

nwds=5*ntemp*nbin

*d purr.138

nwds=nbin*ntemp

call reserv('tval',nwds,itval,a)

*d purr.228

nw=1+5*ntemp*nbin

*d purr.409

nw=1+5*ntemp*nbin

*d purr.415,424

do i=1,5

do j=1,nbin

n=n+1

a(n)=sigfig(a(itabl-1+j+nbin*(i-1)+5*(it-1)*nbin),7,0)

enddo

enddo

*d purr.1730,1731

dimension bkg(4),sig0(nsig0),tval(nbin,ntemp)

dimension sigf(5,10,10),tabl(nbin,5,ntemp)

*i purr.1743

dimension tmin(10),tmax(10),tsum(10)

*i purr.1794

do itemp=1,ntemp

do i=1,nsig0

do j=1,8

bval(j,i,itemp)=0

enddo

enddo

enddo

*i purr.2163

c

c     ***loop over temperatures

c     ***using a different total cross section bin structure for each

do 140 itemp=1,ntemp

*d purr.2169

es(ie)=els(itemp,ie)+fis(itemp,ie)+cap(itemp,ie)+bkg(1)

*d purr.2172,2173

tmin(itemp)=es(1)

tmax(itemp)=es(ne)

nebin=nsamp/(nbin-3.375)

ibin=nebin/16

do i=1,nbin-1

tval(i,itemp)=es(ibin)

if (i.eq.1) ibin=ibin+nebin/4

if (i.gt.1.and.i.lt.nbin-2) ibin=ibin+nebin

if (i.eq.nbin-2) ibin=ibin+nebin/4

if (i.eq.nbin-1) ibin=ibin+nebin/16

enddo

tval(nbin,itemp)=big

*d purr.2174

*d purr.2176,2177

do j=1,5

tabl(i,j,itemp)=0

*d purr.2180,2195

tsum(itemp)=0

*d purr.2200

tot=els(itemp,ie)+fis(itemp,ie)+cap(itemp,ie)+bkg(1)

*d purr.2201,2203

if (tot.lt.tmin(itemp)) tmin(itemp)=tot

if (tot.gt.tmax(itemp)) tmax(itemp)=tot

call fsrch(tot,tval(1,itemp),nbin,ii,mfl)

*d purr.2206,2228

tsum(itemp)=tsum(itemp)+1

tabl(ii,1,itemp)=tabl(ii,1,itemp)+1

tabl(ii,2,itemp)=tabl(ii,2,itemp)+tot

tabl(ii,3,itemp)=tabl(ii,3,itemp)+els(itemp,ie)+bkg(2)

tabl(ii,4,itemp)=tabl(ii,4,itemp)+fis(itemp,ie)+bkg(3)

tabl(ii,5,itemp)=tabl(ii,5,itemp)+cap(itemp,ie)+bkg(4)

do i=1,nsig0

tem=sig0(i)/(sig0(i)+tot)

bval(1,i,itemp)=bval(1,i,itemp)+tot*tem

bval(2,i,itemp)=bval(2,i,itemp)

&        +(els(itemp,ie)+bkg(2))*tem

bval(3,i,itemp)=bval(3,i,itemp)

&        +(fis(itemp,ie)+bkg(3))*tem

bval(4,i,itemp)=bval(4,i,itemp)

&        +(cap(itemp,ie)+bkg(4))*tem

bval(5,i,itemp)=bval(5,i,itemp)+tot*tem*tem

bval(6,i,itemp)=bval(6,i,itemp)+tem

bval(7,i,itemp)=bval(7,i,itemp)+tem*tem

enddo

*i purr.2229

c

c     ***close loop over temperatures

140 continue

*d purr.2296,2299

*d purr.2301,2309

*d purr.2311,2315

tmin(itemp)=tmin(itemp)+tnorm

tval(nbin,itemp)=tmax(itemp)

denom=tabl(i,1,itemp)

if (denom.eq.zero) denom=1

tabl(i,1,itemp)=tabl(i,1,itemp)/tsum(itemp)

tabl(i,2,itemp)=tabl(i,2,itemp)/denom

tabl(i,3,itemp)=tabl(i,3,itemp)/denom

tabl(i,4,itemp)=tabl(i,4,itemp)/denom

tabl(i,5,itemp)=tabl(i,5,itemp)/denom

tabl(i,2,itemp)=tabl(i,2,itemp)-tnorm

tabl(i,3,itemp)=tabl(i,3,itemp)-enorm

tabl(i,4,itemp)=tabl(i,4,itemp)-fnorm

tabl(i,5,itemp)=tabl(i,5,itemp)-cnorm

*d purr.2318,2321

*d purr.2325,2332

do itemp=1,ntemp

do ixx=1,4

if (ixx.eq.1) then

write(nsyso,

&           '('' tmax'',1p,e11.3,1p,10e11.3/(16x,10e11.3))')

&           temp(itemp),(tval(i,itemp),i=1,nbin)

write(nsyso,

&           '('' prob'',1p,e11.3,1p,10e11.3/(16x,10e11.3))')

&           temp(itemp),(tabl(i,1,itemp),i=1,nbin)

endif

write(nsyso,'(1x,a,1x,1p,e11.3,10e11.3/(16x,10e11.3))')

&        nmr(ixx),temp(itemp),(tabl(i,ixx+1,itemp),i=1,nbin)

enddo

*d purr.2347

*d purr.2349,2357

if (tabl(j,1,itemp).ne.zero) then

den=sig0(i)/(sig0(i)+tabl(j,2,itemp))

ttt=tabl(j,1,itemp)

bval(1,i,itemp)=bval(1,i,itemp)

&              +ttt*tabl(j,2,itemp)*den

bval(2,i,itemp)=bval(2,i,itemp)

&              +ttt*tabl(j,3,itemp)*den

bval(3,i,itemp)=bval(3,i,itemp)

&              +ttt*tabl(j,4,itemp)*den

bval(4,i,itemp)=bval(4,i,itemp)

&              +ttt*tabl(j,5,itemp)*den

bval(5,i,itemp)=bval(5,i,itemp)

&              +ttt*tabl(j,2,itemp)*den*den

*d purr.2383

*d purr.2385

&           tabl(j,i,itemp)=tabl(j,i,itemp)*sigi(i-1)

&           /sigf(i-1,1,itemp)

*ident up85

*/ heatr -- 25feb02

*/  add mt=442 to hold the total photon production ev-barns

*i heatr.66

c     *               442   total photon ev-barns                      *

*i heatr.835

npkkk=0

do ipk=3,npk

if (mtp(ipk).eq.442) npkkk=ipk

enddo

*i heatr.1145

if (izap.eq.0.and.npkkk.gt.0) c(npkkk)=c(npkkk)+h

*d heatr.1199

if (mtp(index).lt.442) c(index)=c(index)+h+ebal6

*i heatr.1270

if (mtp(index).eq.442) go to 286

*i heatr.1332

c         442=total photon ev-barns in kerma

*i heatr.1350

if (mtpi.eq.442) iflag=1

*d heatr.4625

if (mtp(index).lt.442) c(index)=c(index)+h

if (mtp(index).eq.442) c(index)=c(index)-h

*d heatr.4657,4659

if (mtp(index).lt.442) c(index)=c(index)+h

if (mtp(index).eq.442) c(index)=c(index)-h

*d heatr.5041

if (mtp(i).ge.442) then

*ident up86

*/ leapr -- 10dec02

*/   add the fcc lattices for aluminum and lead to the

*/   coherent scattering option.

*i leapr.97

c     *                   4  aluminum                                  *

c     *                   5  lead                                      *

c     *                   6  iron                                      *

*d leapr.380

maxb=60000

*i leapr.2407

data al1,al3,al4/4.04d-8,26.7495d0,1.495/

data pb1,pb3,pb4/4.94d-8,207.d0,1.d0/

data fe1,fe3,fe4/2.86d-8,55.454d0,12.9d0/

data twothd/0.666666666667d0/

*i leapr.2414

data al1,al3,al4/4.04e-8,26.7495e0,1.495/

data pb1,pb3,pb4/4.94e-8,207.e0,1.e0/

data fe1,fe3,fe4/2.86e-8,55.454e0,12.e0/

data twothd/0.666666666667e0/

*i leapr.2419

taufcc(m1,m2,m3)=c1*(m1*m1+m2*m2+m3*m3+twothd*m1*m2

&  +twothd*m1*m3-twothd*m2*m3)*twopis

taubcc(m1,m2,m3)=c1*(m1*m1+m2*m2+m3*m3+m1*m2+m2*m3+m1*m3)*twopis

*i leapr.2450

else if (lat.eq.4) then

c        aluminum

a=al1

amsc=al3

scoh=al4/natom

else if (lat.eq.5) then

c        lead

a=pb1

amsc=pb3

scoh=pb4/natom

else if (lat.eq.6) then

c        iron

a=fe1

amsc=fe3

scoh=fe4/natom

*d leapr.2454,2456

if (lat.lt.4) then

c1=4/(3*a*a)

c2=1/(c*c)

scon=scoh*(4*pi)**2/(2*a*a*c*sqrt3*econ)

else if (lat.ge.4.and.lat.le.5) then

c1=3/(a*a)

scon=scoh*(4*pi)**2/(16*a*a*a*econ)

else if (lat.eq.6) then

c1=2/(a*a)

scon=scoh*(4*pi)**2/(8*a*a*a*econ)

endif

*d leapr.2463

c     ***compute lattice factors for hexagonal lattices

if (lat.gt.3) go to 210

*i leapr.2553

go to 220

c

c     ***compute lattice factors for fcc lattices

210 if (lat.gt.5) go to 215

phi=ulim/twopis

i1m=int(a*sqrt(phi))

i1m=15

k=0

do i1=-i1m,i1m

i2m=i1m

do i2=-i2m,i2m

i3m=i1m

do i3=-i3m,i3m

tsq=taufcc(i1,i2,i3)

if (tsq.gt.zero.and.tsq.le.ulim) then

tau=sqrt(tsq)

w=exp(-tsq*t2*wint)/tau

f=w*formf(lat,i1,i2,i3)

k=k+1

if ((2*k).gt.nw) call error('coh',

&               'storage exceeded',' ')

b(ifl+2*k-2)=tsq

b(ifl+2*k-1)=f

endif

enddo

enddo

enddo

imax=k-1

go to 220

c

c     ***compute lattice factors for bcc lattices

215 continue

phi=ulim/twopis

i1m=int(a*sqrt(phi))

i1m=15

k=0

do i1=-i1m,i1m

i2m=i1m

do i2=-i2m,i2m

i3m=i1m

do i3=-i3m,i3m

tsq=taubcc(i1,i2,i3)

if (tsq.gt.zero.and.tsq.le.ulim) then

tau=sqrt(tsq)

w=exp(-tsq*t2*wint)/tau

f=w*formf(lat,i1,i2,i3)

k=k+1

if ((2*k).gt.nw) call error('coh',

&               'storage exceeded',' ')

b(ifl+2*k-2)=tsq

b(ifl+2*k-1)=f

endif

enddo

enddo

enddo

imax=k-1

c

c     ***sort lattice factors

220 do i=1,imax

jmin=i+1

do j=jmin,k

if (b(ifl+2*j-2).lt.b(ifl+2*i-2)) then

st=b(ifl+2*i-2)

sf=b(ifl+2*i-1)

b(ifl+2*i-2)=b(ifl+2*j-2)

b(ifl+2*i-1)=b(ifl+2*j-1)

b(ifl+2*j-2)=st

b(ifl+2*j-1)=sf

endif

enddo

enddo

k=k+1

b(ifl+2*k-2)=ulim

b(ifl+2*k-1)=b(ifl+2*k-3)

nw=2*k

*i leapr.2600

c           lat=4,5  fcc lattice (aluminum, lead)

c           lat=6    bcc lattice (iron)

*i leapr.2626

else if (lat.eq.4.or.lat.eq.5) then

c        fcc lattices.

e1=2*pi*l1

e2=2*pi*(l1+l2)

e3=2*pi*(l1+l3)

formf=(1+cos(e1)+cos(e2)+cos(e3))**2

&     +(sin(e1)+sin(e2)+sin(e3))**2

else if (lat.eq.6) then

c        bcc lattices.

e1=2*pi*(l1+l2+l3)

formf=(1+cos(e1))**2+(sin(e1))**2

*ident up87

*/ acer -- 2jul03

*/  the mt numbers used for determining charged particle production

*/  have some errors.  this affects some light-isotope runs for

*/  incident charged particles.

*d acer.4770,4771

if (mt.eq.5.or.mt.eq.28.or.mt.eq.41.or.

&              mt.eq.42.or.mt.eq.44.or.mt.eq.45.or.

*d acer.4785

if (mt.eq.5.or.mt.eq.32.or.mt.eq.35.or.

*d acer.4798

if (mt.eq.5.or.mt.eq.33.or.mt.eq.36.or.

*d acer.4811

if (mt.eq.5.or.mt.eq.34.or.mt.eq.106.or.

*d acer.4823,4825

if (mt.eq.5.or.(mt.ge.22.and.mt.le.25).or.

&              mt.eq.29.or.mt.eq.30.or.

&              mt.eq.35.or.mt.eq.36.and.mt.eq.45.or.

*d acer.5024

if (mt.eq.2.or.mt.eq.5.or.mt.eq.28.or.mt.eq.41.or.

&        mt.eq.42.or.mt.eq.44.or.mt.eq.45.or.

*d acer.5031

if (mt.eq.2.or.mt.eq.5.or.mt.eq.32.or.mt.eq.35.or.

*d acer.5036

if (mt.eq.2.or.mt.eq.5.or.mt.eq.33.or.mt.eq.36.or.

*d acer.5041

if (mt.eq.2.or.mt.eq.5.or.mt.eq.34.or.mt.eq.106.or.

*d acer.5045

if (mt.eq.2.or.mt.eq.5.or.(mt.ge.22.and.mt.le.25).or.

*d acer.5047

&        mt.eq.35.or.mt.eq.36.and.mt.eq.45.or.

*d acer.5130

if (mt.eq.2.or.mt.eq.5.or.mt.eq.28.or.mt.eq.41.or.

&        mt.eq.42.or.mt.eq.44.or.mt.eq.45.or.

*d acer.5137

if (mt.eq.2.or.mt.eq.5.or.mt.eq.32.or.mt.eq.35.or.

*d acer.5142

if (mt.eq.2.or.mt.eq.5.or.mt.eq.33.or.mt.eq.36.or.

*d acer.5147

if (mt.eq.2.or.mt.eq.5.or.mt.eq.34.or.mt.eq.106.or.

*d acer.5153

&        mt.eq.35.or.mt.eq.36.and.mt.eq.45.or.

*/ acer -- 02jul03

*/  for the particle production sections, the acer logic fails for

*/  some cases where two identical particles are produced by

*/  file 6, such as p+t->alpha+alpha.  the acer job seems to run

*/  ok, but it fails when the file is read back in for checking

*/  and plotting.  this patch fixes the problem.  this problem

*/  only shows up for a few light-isotope cases with incident

*/  charged particles.

*d acer.224

&  nprod,kprod(300),mprod(300),iprod(300),lprod(300)

*d acer.551

&  nprod,kprod(300),mprod(300),iprod(300),lprod(300)

*i acer.741

lprod(nprod)=0

*i acer.746

lprod(nprod)=0

*i acer.751

lprod(nprod)=0

*i acer.756

lprod(nprod)=0

*i acer.761

lprod(nprod)=0

*i acer.766

lprod(nprod)=0

*i acer.929

lprod(nprod)=ik

*i acer.937

lprod(nprod)=ik

*i acer.945

lprod(nprod)=ik

*i acer.953

lprod(nprod)=ik

*i acer.961

lprod(nprod)=ik

*i acer.969

lprod(nprod)=ik

*d acer.980,981

isort1=100000*mprod(i)+10*iprod(i)+lprod(j)

isort2=100000*mprod(j)+10*iprod(j)+lprod(j)

*i acer.985

isave4=lprod(j)

*i acer.991

lprod(i)=isave4

*d acer.8061

&  nprod,kprod(300),mprod(300),iprod(300),lprod(300)

*d acer.8259

if (ik.eq.lprod(j)) then

*d acer.8662

if (ik.eq.lprod(j)) then

*d acer.8671

if (ik.eq.lprod(j).and.law.eq.4) then

*d acer.8691

if ((ik.eq.lprod(j).and.law.eq.2).or.

*d acer.8819

else if (ik.eq.lprod(j).and.law.eq.7) then

*d up36.7

if (ik.ne.lprod(j).or.law.ne.1) then

*i up20.56

c

c                    ***skip if not correct subsection

else if (ik.ne.lprod(j)) then

call skip6a(nin,0,0,a(iscr),law)

*/ acer -- 02jul03

*/  patch the phase-space option for the primary particle.  this

*/  problem showed up for the proton distribution for 3He(p,2p).

*d acer.6582,6583

test1=one+one/100000

test2=one/10-one/1000000

test3=one-one/100000

do while (xx.lt.test1)

*d acer.6585,6587

if (xx.lt.test2) then

*d acer.6603,6604

do while (xx.lt.test1)

*d acer.6606,6607

if (xx.gt.test3) then

*d acer.6620,6622

if (xx.lt.test2) then

*ident up88

*/ matxsr -- 28jul03

*/  the update that introduced a photonuclear capability for

*/  matxsr on 12feb02 accidently removed the assignment of the

*/  scratch file used for computing the self-shielding delta

*/  cross section values. any matxs files that include temperature

*/  and sigma-zero data and that were generated with versions of

*/  njoy99 from 99.67 up are incorrect.

*i matxsr.440

nscrt7=16

*/  the read statement that brings in the group structures has a

*/  scale factor in it by mistake.  this distorts group energies

*/  that are written on the gendf tape in f format.  the result is

*/  an incorrect group structure on the matxs file.  this error

*/  has existed for many years without causing problems.

*d matxsr.2291

read(nin,'(6e11.0)') (a(i+nw1),i=1,lim)

*/  more room is need to read in vector cross sections for

*/  187 group runs.  this shows up for delayed-neutron data.

*d matxsr.1488

dimension b(2000)

*d matxsr.1501

maxb=2000

*ident up89

*/ groupr -- 29jul03

*/  increase the main container array to allow for up to p5 for

*/  the lanl u233 evaluation proposed for endf/b-vii.

*d up34.7

dimension a(200000)

*d up34.9

iamax=200000

*/  increase the number of gammas allowed to handle w-182 and

*/  w-186 from endf/b-vi release 8.

*d groupr.7783

dimension loca(550)

*d groupr.7791

data nylmax/550/

*ident up90

*/ purr -- 6aug03

*/  the purr module is zeroing out the lssf and intunr flags in

*/  the section mt=152 that contains the bondarenko selfshielding

*/  information.  this has the dramatic effect giving different

*/  infinitely dilute cross sections when nsigz is one or greater

*/  than one, and incorrectly interpolated values.  note that purr

*/  is substituting its bondarenko values for the ones from unresr

*/  if both unresr and purr are run in that order.  these errors

*/  can have important effects on multigroup results from groupr.

*d purr.337

a(l+2)=lssf

*d purr.340

a(l+5)=2

*ident vers

*/ update the version name and date

*/ to reflect the date of the latest modifications

*d njoy.8,9

c     *    version 99.90                                               *

c     *    06 Aug 03                                                   *

*d njoy.307

data vers/'99.90   '/

*/

## C.2 uplf95

REM uplf95       : for lahey95

*ident x86lf9

*/ ----------------------------------------

*/ machine-dependent changes to njoy99

*/ for x86 machines using

*/ Lahey LF95 with f77-style fixed lines

*/ be sure to use "*set sw"

*/ ----------------------------------------

*d njoy.308,309

data lab/'lanl t-2'/

data mx/'x86lf95'/

*/ provide machine-specific fatal error exit

*d njoy.365,366

stop 77

*/ elapsed time

*d njoy.514

call cpu_time(time)

*/ date

*d njoy.524

character date*8,time*10,zone*5

integer values(8)

intrinsic date_and_time

call date_and_time(date,time,zone,values)

write(hdate,'(i2,''/'',i2,''/'',i2)')

&  values(2),values(3),mod(values(1),100)

*/ wall clock time

*d njoy.537

character date*8,time*10,zone*5

integer values(8)

intrinsic date_and_time

call date_and_time(date,time,zone,values)

write(htime,'(i2,'':'',i2,'':'',i2)')

&  values(5),values(6),values(7)

*/ random numbers

*d njoy.6161

call random_number(rr)

rann=rr

*/ machine constants for slatec functions

*d njoy.5323,5334

*d njoy.5338,5746

c     for absoft f90 using f90 intrinsics

dmach(1)=tiny(1.d0)

dmach(2)=huge(1.d0)

dmach(3)=2.d0**(-digits(1.d0))

dmach(4)=2.d0**(1-digits(1.d0))

dmach(5)=0.30103001d+0

## C.3 upn_Trkov

REM upn_Trkov    : IAEA upn for fendl2.1

REM       - Include: upiaea1, upijs57,upijs59, upijs61, upijs62, upijs63, upijs64

REM         upiaea2 upiaea3, upfendl1,upfndl2, upfndl3, upfndl4, upfndl5, upfndl6

*/

*/ Updates from Trkov

*/

*ident upiaea1

*/ groupr - A.Trkov, IAEA

*/          Local updates from NJOY97 that were not implemented

*/ Need more space for the flux calculator (Case: U-238)

*d up89.6

dimension a(400000)

*d up89.8

iamax=400000

*/

*ident upijs57

*/ groupr  A.Trkov, 9-March-1999

*/ groupr is caught in an infinite loop for Be-9 from ENDF/B-VI

*/ on a PC with Lahey compiler.

*/ It seems the products inside an "if" statements are

*/ computed differently than outside. The program does not

*/ recognise that ep EQUALS "test" when written as a product.

*d groupr.6054

test=shade*epn

if (idis.gt.0.and.ep.lt.test) epn=test

*/

*/ Old proposal from C.Dean

*d groupr.2745,2746

b(iz+3+li)=(sigz(iz)-sam)*wtf*(1-beta)

*/

*ident upijs59

*/ acer   A.Trkov 20-aug-1999

*/ If pointwise representation in CM system, csn should be used

*/ (pointed out by Harry Wienke).

*d acer.3394,3396

if (csn.ge.a(ll).and.csn.le.a(ll+2))

&                    call terp1(a(ll),a(ll+1),a(ll+2),a(ll+3),

&                    csn,fmu,lang-10)

*/

*ident upijs61

*/ acer   A.Trkov 3-dec-1999

*/        fix6 may run out of space without warning

*d acer.3247

dimension a(2000)

*d up3.38

data namax/2000/

*i acer.3262

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3272

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3278

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3280

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3282

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3284

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3290

if(nw.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3296

if(nw+l.gt.namax) call error('fix6','storage exceeded.',' ')

*i acer.3299

if(nw+l.gt.namax) call error('fix6','storage exceeded.',' ')

*/

*ident upijs62

*/ groupr  A.Trkov, 29-Apr-2002

*/         - Fix inconsistent usage of output weighting flux unit number

*/         - Fix logic when searching for the right flux point

*i groupr.80

c     *            note: weighting flux file is always written binary  *

*d groupr.99

c     *    ninwt   tape unit for flux parameters (binary)              *

*d groupr.272

*d groupr.2290

ninwt=iabs( ninwt)

call openz(-ninwt,1)

*d groupr.2294

&     ehi,sigpot,nflmax,-ninwt,jsigz

*d groupr.2307,2308

call openz(-ninwt,0)

write(nsyso,'(/'' ninwt......'',i4)') -ninwt

*d groupr.3037

if (e.gt.el*(1-small).and.e.lt.en*(1+small)) go to 230

*/

*ident upijs63

*/ purr  A.Trkov, May 2002

*/       Increase scratch space to process Pu-239 from JEF-2.2

*d purr.95

maxscr=12000

*/

*ident upijs64

*/ groupr  A.Trkov, July 2002

*/         There is an error in Cl-37 in ENDF/B-VI Rev.8

*/         MAT 1731 MF 15 MT 102

*/         The first energy for the gamma yields is zero. It

*/         redefines enext in getsed to zero, which is

*/         interpreted as a flag to do initialisation in

*/         getgyl (called from getff). Since 'yl' is

*/         already reserved, groupr crashes.

*d groupr.8697

if (elo.gt.0 .and. elo.lt.enext) enext=elo

*/

*ident upiaea2

*/ groupr - A.Trkov, IAEA, Feb-2003

*/          Increase array size for Legendre coefficients

*i groupr.4756

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.4764

dimension term(mxlg),terml(mxlg)

*i groupr.5209

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.5212

dimension term(mxlg),x(10),y(10,mxlg)

*d groupr.5329,5330

c     maximum legendre coefficients

parameter (mxlg=65)

dimension cnow(*),term(*),p(mxlg)

dimension x(10),y(10,mxlg),yt(mxlg)

*d groupr.5333

external f6ddx,f6psp,f6dis,legndr,error

*i groupr.5358

if(nl.gt.mxlg) call error('f6cm','nl>mxlg',' ')

*d groupr.5586

c     maximum legendre coefficients

parameter (mxlg=65)

dimension cnow(*),p(mxlg)

*d groupr.5768

c     maximum legendre coefficients

parameter (mxlg=65)

dimension cnow(*),p(mxlg)

*i groupr.5630

if(nl.gt.mxlg) call error('f6ddx','nl>mxlg',' ')

*i groupr.5992

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.5995

dimension term(mxlg),p(mxlg),amu(50),fmu(50),qp(8),qw(8)

*i groupr.6130

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.6133,6134

dimension term1(mxlg),term2(mxlg),p(mxlg)

dimension qp(8),qw(8)

*i groupr.6733

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.6740

dimension flo(mxlg),fhi(mxlg)

*i groupr.7314

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.7318

dimension b(6),alo(mxlg),ahi(mxlg)

*i groupr.7929

c     maximum legendre coefficients

parameter (mxlg=65)

*d groupr.7942

dimension fl(mxlg)

*/

*ident upiaea3

*/ acer   - A.Trkov, IAEA, Feb-2003

*/          declare "error" external to avoid conflict with intrinsic function

*i up69.66

external error

*/

*ident upfndl1

*/ matxsr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ Need more space  (Case: 1-H-2 from JENDL-3.3)

*/  subroutine band

*d matxsr.1973

dimension b(5000)

*d matxsr.1978

maxb=5000

*/  subroutine shufl

*d matxsr.2078

dimension b(5000)

*d matxsr.2080

maxb=5000

*/

*ident upfndl2

*/ gaspr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ Need more space (case Ni-058 from JEFF-3.0)

*d gaspr.28

dimension egas(80000),sgas(5,80000)

*d gaspr.41

maxg=80000

*ident upfndl3

*/ purr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ to allow PT for multi-isotope materials when

*/ not all the isotopes have unresolved resonance data

*d purr.624

*i purr.651

if (ier.eq.ner) go to 110

*/

*ident upfndl4

*/ acer - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ Format extension for negative energies (overlap)

*d acer.4947,4948

write(nsyso,'(''   energy range: '',1p,e11.4,

&        '' - '',e11.4,'' ev'')') urlo,urhi

*/

*ident upfndl5

*/ groupr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ Needed to process Be-9 from JEFF-3.0 evaluation

*/  MT=875-891 for (n,2n) splitted reaction

*i groupr.1147

else if (mtd.ge.875.and.mtd.le.884) then

write(reac,'(''2n0'',i1)') mtd-875

else if (mtd.ge.885.and.mtd.le.890) then

write(reac,'(''2n'',i2)') mtd-875

else if (mtd.eq.891) then

reac='2nc'

*i groupr.3964

if (iverf.ge.6.and.mtd.ge.875.and.mtd.le.891) mt=mtd

*i groupr.4331

if (mfd.ge.31.and.mfd.le.36.and.iverf.ge.6.and.

&   (mtd.ge.875.and.mtd.lt.891)) go to 400

*i groupr.8014

if (mth.ge.875.and.mth.lt.891) za2=1

*i groupr.8330

if (iverf.ge.6.and.mth.ge.875.and.mth.le.890) mt0=875

*/

*/ matxsr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ Needed to process Be-9 from JEFF-3.0 evaluation

*/  MT=875-891 for (n,2n) splitted reaction

*d matxsr.1418

290 if (mt.gt.891) go to 300

*i matxsr.1433

if (mt.ge.875.and.mt.lt.885) write(strng,'(''2n0'',i1)') mt-875

if (mt.ge.885.and.mt.lt.891) write(strng,'(''2n'',i2)') mt-875

if (mt.eq.891) write(strng,'(''2ncn'')')

*i matxsr.1504

k016=0

*i matxsr.1652

if (mt.eq.16) k016=1

if (k016.eq.1.and.mt.ge.875.and.mt.le.891) go to 310

*/

*ident upfndl6

*/ groupr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ subroutine namer corrected for mt=659, reac=d09

*/ It's only affect groupr printout

*d groupr.1124

else if (mtd.ge.650.and.mtd.le.659) then

*/

## C.4 upn_Mattes

REM upn_Mattes   : Thermal Scattering Libraries

REM   - Include:  up3_thermr, up1_leapr, up2_leapr, up3_leapr, up4_leapr,

REM               up5_leapr, up_acer

REM                  Modifications in common/xsst/

REM                - Do not include: up_thermr (updated in upn_Aldama)

*/ Additional updates needed to process JEFF-3.1T2

*/

*/ Updates from Mattes

*/

*ident up_thermr

*/ thermr - M. Mattes/IKE ---------------------------------------mm

*/    increase array size for IKE evaluations

*d thermr.101

dimension a(800000)

*d thermr.131

namax=800000

*/

*/ This section is included in upn_Aldama

*/

*/ */    fix reading long TAB1 records

*/ *i thermr.1543

*/       ll=loc

*/       do while (nb.ne.0)

*/         ll=ll+nw

*/         call moreio(nendf,0,0,a(ll),nb,nw)

*/       enddo

*/ *i thermr.1602

*/       ll=loc

*/       do while (nb.ne.0)

*/         ll=ll+nw

*/         call moreio(nendf,0,0,a(ll),nb,nw)

*/       enddo

*/ */

*/ ------------------------------------------------------------mm

*/ident up2_thermr

*/    maximum.energy transfer at higher temperatures (print only)

*i thermr.1622

if (lat.eq.1) tmax=tmax*tevz/(bk*temp)

*/ ---------------------------------------------------end up2_thermr

*ident up3_thermr

*/   more incident energies necessary for ZrH for an adequate

*/   represention of the neutron scattering xs in comparison

*/   with experimental results (.1 < E_i < 1 eV)

*d thermr.1422,thermr.1423

dimension egrid(79)

dimension ubar(79)

*d thermr.1427

data ngrid/79/

*d thermr.1433,thermr.1436

&  .030613d0,.042757d0,.056925d0,.081972d0,

*      .1d0, .111573d0, .12d0, .13d0, .145728d0, .16d0, .17d0,

&  .184437d0,

*    .195d0, .2277d0, .24d0, .2510392d0,.2705304d0,.2907501d0,

&  .3011332d0,.3206421d0,.3576813d0,

*   .38d0, .4d0, .4170351d0,  .44d0, .48d0, .5032575d0, .53d0,

&   .56d0, .59d0,  .6249328d0, .65d0, .69d0, .72d0, .75d0,

*   .7821141d0, .82d0, .89d0, .9506956d0,1.0137432d0,1.1664337d0,

*d thermr.1455,thermr.1458

&  .030613e0,.042757e0,.056925e0,.081972e0,

*      .1e0, .111573e0, .12e0, .13e0, .145728e0, .16e0, .17e0,

&  .184437e0,

*    .195e0, .2277e0, .24e0, .2510392e0,.2705304e0,.2907501e0,

&  .3011332e0,.3206421e0,.3576813e0,

*   .38e0, .4e0, .4170351e0,  .44e0, .48e0, .5032575e0, .53e0,

&   .56e0, .59e0,  .6249328e0, .65e0, .69e0, .72e0, .75e0,

*   .7821141e0, .82e0, .89e0, .9506956e0,1.0137432e0,1.1664337e0,

*/

*/ --------------------------------------------------end up3_thermr

*ident up1_leapr

*/

*/ if number(>200) for alpha and/or beta values then

*/           increase array sizes plus working buffers

*/    e.g. beta(200) -> beta(400) for H2O

*d leapr.164

common/ab/nalpha,nbeta,naint,nbint,alpha(200),beta(400)

*d leapr.173

common/lstore/a(7500000)

*d leapr.178

data nbmax,namax/400,200/

*d leapr.189

maxa=7500000

*d leapr.391

mscr=4000

*d leapr.420

common/ab/nalph1,nbeta1,naint,nbint,alph1(200),beta1(400)

*d leapr.426

dimension maxt(400)

*d leapr.794

common/ab/nalpha,nbeta,naint,nbint,alpha(200),beta1(400)

*d leapr.1252

common/ab/nalpha1,nbeta1,naint,nbint,alpha(200),beta1(400)

*d leapr.1852

common/ab/nalph1,nbeta1,naint,nbint,alpha(200),beta1(400)

*/

*/    IKE evaluation of H(H2O) creates more pairs of alpha

*/    and S(alpha,beta) than npage

*i leapr.3122

l_mm=1+nw

do while (nb.ne.0)

call moreio(0,nout,nprnt,scr(l_mm),nb,nw)

l_mm=l_mm+nw

enddo

*/ -------------------------------------------------end up1_leapr

*ident up2_leapr

*/     for H(H2O), D(D2O) NS should be equal 1

*d leapr.2976,2977

if(nss.gt.0) scr(5)=6*(nss+1)

scr(6)=nss

*/ -------------------------------------------------end up2_leapr

*ident up3_leapr

*/  T-eff calculation

*d leapr.1557

tempf(itemp)=(tbeta+twt)*tempf(itemp)+tsave

*/ -------------------------------------------------end up3_leapr

*ident up4_leapr

*/ generation of more than 10 temperatures

*d leapr.166,167

common/te/tempr(20),tempf(20),tempf1(20)

common/dw/dwpix(20),dwp1(20)

*d leapr.179

data ntmax/20/

*d leapr.600,601

common/te/tempr(20),tempf(20),tempf1(20)

common/dw/dwpix(20),dwp1(20)

*d leapr.797

common/te/tempr(20),tempf(20),tempf1(20)

*d leapr.1256

common/te/tempr(20),tempf(20),tempf1(20)

*d leapr.1258

common/dw/dwpix(20),dwp1(20)

*d leapr.1856

common/te/tempr(20),tempf(20),tempf1(20)

*d leapr.2651.2652

common/te/tempr(20),tempf(20),tempf1(20)

common/dw/dbw(20),dbw1(20)

*/ --------------------------------------------------end up4_leapr

*ident up5_leapr

*/   correct directory

*i leapr.2797

scr(5)=scr(5)+1

if(iel.ne.0) scr(5)=scr(5)+1

*/ --------------------------------------------------end up5_leapr

*/

*ident up_acer

*/ id-name of thermal data set with 6 characters else blank

*i acer.358

if (nch.eq.0) nch=6

*/

*/ more than 64 bins  wt(65)

*d acer.13079

dimension wt(401)

*/

*/ increase of scratch buffer (?)

*d acer.13098

ninmax=8000

*/

*/ ------------------------------------------------jan05------end

## C.5 upn_Aldama

REM upn_Aldama   : up_therm1 update included in upn_Mattes (included in upn_ADS)

*/ Changes in up1_thermr by M.Mattes

*/

*/ Equivalent to up_thermr in upn_Mattes

*/

*ident wlup2

*/ */ thermr - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/ */ More space for new scattering law

*/ *d thermr.101

*/       dimension a(800000)

*/ *d thermr.131

*/       namax=800000

*/

*/ subroutine calcem - D. L. Aldama, NDS/IAEA Consultant, Nov-2004

*/  TAB1 records are larger than npage=306

*/  moreio should be used

*/  required by thermal scattering law generated by NDS/IKE

*/

*d thermr.1543

lmore=loc

call tab1io(nendf,0,0,a(loc),nb,nw)

do while (nb.ne.0)

lmore=lmore+nw

call moreio(nendf,0,0,a(lmore),nb,nw)

enddo

*d thermr.1572

lmore=loc

call listio(nendf,0,0,a(loc),nb,nw)

do while (nb.ne.0)

lmore=lmore+nw

call moreio(nendf,0,0,a(lmore),nb,nw)

enddo

*d thermr.1598

lmore=loc

call listio(nendf,0,0,a(loc),nb,nw)

do while (nb.ne.0)

lmore=lmore+nw

call moreio(nendf,0,0,a(lmore),nb,nw)

enddo

*d thermr.1602

lmore=loc

call tab1io(nendf,0,0,a(loc),nb,nw)

do while (nb.ne.0)

lmore=lmore+nw

call moreio(nendf,0,0,a(lmore),nb,nw)

enddo

*/

## C.6 upn_Hogenbirk

REM upn_Hogenbirk: Delayed neutrons in ACE format for JEFF31.

REM               - Include: nrg_a50, nrg_a52, nrg_a57, nrg_re15 (dla1 in upn_ADS)

*/

*/ NRG updates for ACER-processing of delayed neutron data

*/

*ident nrg_a50

*/ acer -- 21sep2001 A. Hogenbirk (NRG)

*/ -----------------------------------------------

*/          allow processing of delayed nu data

*/          for use in MCNP (version 4C onwards)

*/ -----------------------------------------------

*/

*d acer.2194

&     (mf.eq.5.and.mt.gt.91.and.mt.ne.455)) then

*i acer.4671

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

*i acer.4673

dimension nus(3)

*i acer.4681

nus(1)=452

nus(2)=455

nus(3)=456

*i acer.4744

nnud=0

*d acer.4846

nnus=1

mta=nus(nnus)

*i acer.4856

if (mta.eq.455) call reserv('nud',nw,inud,a)

*i acer.4858

if (mta.eq.455) in=inud

*i acer.4866

if (mta.eq.455) nnud=nw

*i acer.4869

if (mta.eq.455) then

c

c read and store delayed data

c

call listio(nin,0,0,a(iscr),nb,nw)

nnfd=nint(a(iscr+4))

nw=nnfd

call reserv('lambdel',nw,ilambdel,a)

in=ilambdel

nlambdel=nw

do i=1,nlambdel

a(in+i-1)=a(iscr+i+5)

enddo

endif

*i acer.4883

if (mta.eq.455) call reserv('nud',nw,inud,a)

*i acer.4885

if (mta.eq.455) in=inud

*i acer.4904

if (mta.eq.455) nnud=nw

*d acer.4907

if (mta.eq.456.or.kfis.eq.1) idone=1

nnus=nnus+1

if (nnus.gt.3) then

idone=1

else

mta=nus(nnus)

endif

*d acer.4908

*i acer.4909

c      write(nsyso,*)  'inu  = ', inu

c      write(nsyso,*)  'inud = ', inud

c      write(nsyso,*)  'inup = ', inup

*i acer.5275

c      write(nsyso,*)  'mtr  = ', mtr

c      write(nsyso,*)  'lqr  = ', lqr

c      write(nsyso,*)  'tyr  = ', tyr

c      write(nsyso,*)  'lsig = ', lsig

c      write(nsyso,*)  'ir   = ', ir

*i acer.5324

c      write(nsyso,*)  'land = ', land

c      write(nsyso,*)  'and  = ', and

*i acer.5515

c

c     ***store delayed fission energy distribution data

c     ***after unresolved-range probability tables and before

c     ***gamma data

c

c     ***this location is essential...

c

if (nnud.ne.0) then

c

c store delayed nu

c

c        write(nsyso,*)  'next = ', next

dnu=next

do i=1,nnud

xss(next)=a(i-1+inud)

next=next+1

enddo

c        write(nsyso,*)  'next = ', next

c

c store basic data

c

bdd=next

c        write(nsyso,*)  'bdd =', bdd

call acelf5bd(next,1,matd,455,q,nin)

c        write(nsyso,*)  'next = ', next

c

c

ldlwnud=next

next=ldlwnud+nnfd

dlwnud=next

c        write(nsyso,*)  'ldlwnud =', ldlwnud

c        write(nsyso,*)  'dlwnud =', dlwnud

c

c process delayed neutron energy distributions

c

call acelf5d(next,1,matd,455,q,nin)

c          write(nsyso,*)  'i    = ', i

c          write(nsyso,*)  'next = ', next

endif

c

*i acer.5938

subroutine acelf5bd(next,i,matd,mt,q,nin)

c     *****************************************************************

c     process basic delayed neutron data from file 5.

c     *****************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

integer esz,sig,and,tyr,dlw,gpd,fis,sigp,andp,dlwp,yp,end

common/jxst/esz,nu,mtr,lqr,tyr,lsig,sig,land,and,ldlw,dlw,

&  gpd,mtrp,lsigp,sigp,landp,andp,ldlwp,dlwp,yp,fis,end,

&  iurpt,jxsd(9)

common/lsize/max1,max2,max3

common/xsst/xss(4000000),n3   ! NEA changes

common/mainio/nsysi,nsyso,nsyse,ntty

common/cont/c1h,c2h,l1h,l2h,n1h,n2h,math,mfh,mth,nsh,nsp,nsc

common/ace1/tempd,err,matdd,nbina,nbinp,negn,iprint,iopt,ndigit

common/astore/a(80000)

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

character*60 strng

character*26 messs

dimension xs(20),ys(20),xxs(200),yys(200)

external findex,findf,contio,tab1io,error,moreio,tosend

external sigfig

data ismax/20/, jsmax/200/

*if sw

data emev/1.d6/

data tshake/1.d8/

data tol/.02d0/

data tmin/1.d-12/

data rmin/1.d-30/

*else

data emev/1.e6/

data tshake/1.e8/

data tol/.02e0/

data tmin/1.e-12/

data rmin/1.e-30/

*endif

zero=0

c

c     ***find desired reaction

call findex('scr',iscr,a)

call repoz(nin)

call findf(matd,5,mt,nin)

call contio(nin,0,0,a(iscr),nb,nw)

nk=nint(a(iscr+4))

c

c      write(nsyso,*)  'nk =', nk

c

c     ***store each subsection

do k=1,nk

c

c     ***store delay time of this group (per shake)

xss(next)=sigfig(a(ilambdel+k-1)/tshake,ndigit,0)

c         write(nsyso,*)  'delay =', xss(next)

next=next+1

call tab1io(nin,0,0,a(iscr),nb,nw)

u=a(iscr)

lf=nint(a(iscr+3))

m=nint(a(iscr+4))

n=nint(a(iscr+5))

c

c         write(nsyso,*)  'k =', k

c         write(nsyso,*)  'u =', u

c         write(nsyso,*)  'lf =', lf

c         write(nsyso,*)  'm =', m

c         write(nsyso,*)  'n =', n

c

c

if (next+2*m+2*n+3.gt.max3) then

write(messs,'(a,i10,a,i10)') 'maximum = ',max3,

&        ', needed: ',next+2*m+2*n+3

call error('acelf5bd',

&        'storage exceeded.',messs)

endif

c

c

jnt=nint(a(iscr+7))

if (m.ne.1.or.jnt.ne.2) then

ja=next

xss(ja)=m

jb=ja+m

do j=1,m

xss(ja+j)=a(iscr+4+2*j)

xss(jb+j)=a(iscr+5+2*j)

enddo

next=jb+m+1

else

xss(next)=0

next=next+1

endif

xss(next)=n

l=iscr+4+2*m

do j=1,n

xss(j+next)=sigfig(a(2*j+l)/emev,ndigit,0)

xss(j+n+next)=a(2*j+1+l)

enddo

next=next+2*n+1

c

c skip law-dependent data

c

if (lf.eq.1) then

call tab2io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+1.gt.max3) call error('acelf5bd',

&        'insufficient space for energy distributions',' ')

ne=n

do j=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

enddo

c

c        ***law 5...generalized evaporation spectrum

else if (lf.eq.5) then

c            call error('acelf5bd','sorry. acer cannot handle lf=5.',

c     &        'you will have to patch the evaluation to use lf=1.')

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5bd',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

c

c        ***law 7...simple fission spectrum

c        ***law 9...evaporation spectrum

else if (lf.eq.7.or.lf.eq.9) then

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5bd',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

c

c        ***law 11...watt fission spectrum

else if (lf.eq.11) then

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

jnt=nint(a(iscr+7))

if (next+2*m+2*n+2.gt.max3) call error('acelf5bd',

&        'insufficient space for energy distributions',' ')

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5bd',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

c

c        ***law 12...madland-nix fission spectrum

else if (lf.eq.12) then

call tab1io(nin,0,0,a(iscr),nb,nw)

c

c        ***illegal value of lf

else

write(strng,'(''illegal lf='',i2)') lf

call error('acelf5bd',strng,' ')

endif

c

enddo

call tosend(nin,0,0,a(iscr))

return

end

c

c

c

subroutine acelf5d(next,i,matd,mt,q,nin)

c     *****************************************************************

c     process delayed neutron energy spectrum from file 5.

c     *****************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

integer esz,sig,and,tyr,dlw,gpd,fis,sigp,andp,dlwp,yp,end

common/jxst/esz,nu,mtr,lqr,tyr,lsig,sig,land,and,ldlw,dlw,

&  gpd,mtrp,lsigp,sigp,landp,andp,ldlwp,dlwp,yp,fis,end,

&  iurpt,jxsd(9)

common/lsize/max1,max2,max3

common/xsst/xss(4000000),n3    ! NEA changes

common/mainio/nsysi,nsyso,nsyse,ntty

common/cont/c1h,c2h,l1h,l2h,n1h,n2h,math,mfh,mth,nsh,nsp,nsc

common/ace1/tempd,err,matdd,nbina,nbinp,negn,iprint,iopt,ndigit

common/astore/a(80000)

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

character*60 strng

dimension xs(20),ys(20),xxs(200),yys(200)

dimension ein(1000)

external findex,findf,contio,tab1io,error,moreio,tosend

external sigfig

data ismax/20/, jsmax/200/

*if sw

data emev/1.d6/

data tol/.02d0/

data tmin/1.d-12/

data rmin/1.d-30/

*else

data emev/1.e6/

data tol/.02e0/

data tmin/1.e-12/

data rmin/1.e-30/

*endif

zero=0

c

c     ***find desired reaction

call findex('scr',iscr,a)

call repoz(nin)

call findf(matd,5,mt,nin)

call contio(nin,0,0,a(iscr),nb,nw)

nk=nint(a(iscr+4))

c

c     ***store each subsection

do k=1,nk

xss(ldlwnud+k-1)=next-dlwnud+1

call tab1io(nin,0,0,a(iscr),nb,nw)

u=a(iscr)

lf=nint(a(iscr+3))

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+3.gt.max3) call error('acelf5d',

&     'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

if (k.gt.1) xss(last)=next-dlwnud+1

last=next

xss(next)=0

xss(next+1)=lf

if (lf.eq.5) xss(next+1)=4

if (lf.eq.1) xss(next+1)=4

if (lf.eq.12) xss(next+1)=4

if (m.ne.1.or.jnt.ne.2) then

ja=next+3

xss(ja)=m

jb=ja+m

do j=1,m

xss(ja+j)=a(iscr+4+2*j)

xss(jb+j)=a(iscr+5+2*j)

enddo

next=jb+m+1

else

xss(next+3)=0

next=next+4

endif

xss(next)=n

l=iscr+4+2*m

do j=1,n

xss(j+next)=sigfig(a(2*j+l)/emev,ndigit,0)

c            xss(j+n+next)=a(2*j+1+l)

c

c probability should be set to 1.0 at this location:

c it's already included in the bdd block!!

c

*if sw

xss(j+n+next)=1.0d0

*else

xss(j+n+next)=1.0e0

*endif

c

enddo

next=next+2*n+1

xss(last+2)=next-dlwnud+1

c

c        ***store law data according to type

c        ***laws 1, 5, 7, 9, 11 only

c

c        ***law 1...tabulated distributions

if (lf.eq.1) then

*if sw

if (mt.eq.455) q=200.0d0

*else

if (mt.eq.455) q=200.0e0

*endif

call tab2io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+1.gt.max3) call error('acelf5d',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

jnt=mod(jnt,10)

if (jnt.gt.2) jnt=2

if (m.ne.1.or.jnt.ne.2) then

xss(next)=m

do j=1,m

xss(j+next)=a(2*j+4+iscr)

jnt=nint(a(2*j+5+iscr))

jnt=mod(jnt,10)

if (jnt.gt.2) jnt=2

xss(j+m+next)=jnt

enddo

next=next+1+2*m

else

xss(next)=0

next=next+1

endif

xss(next)=n

nextn=next+n

nexd=nextn+n+1

ne=n

do j=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

e=c2h

xss(next+j)=sigfig(e/emev,ndigit,0)

xss(nextn+j)=nexd-dlwnud+1

m=n1h

n=n2h

jnt=nint(a(iscr+5+2*m))

xss(nexd)=jnt

xss(nexd+1)=n

nexd=nexd+1

xss(nexd+1+2*n)=0

do ki=1,n

ep=a(iscr+4+2*m+2*ki)

if (ep.gt.e.and.q.lt.zero) then

write(nsyso,'(/'' ---warning from acelod---'',

&                  6x,''mf5 ep.gt.e with negative q''/

&                  6x,''mt='',i2,'' e='',1p,e12.4,'' ep='',e12.4/

&                  6x,''patching...'')') mt,e/emev,ep/emev

ep=e-(n-ki)*1000

a(iscr+4+2*m+2*ki)=ep

endif

xss(ki+nexd)=sigfig(a(iscr+4+2*m+2*ki)/emev,ndigit,0)

xss(ki+n+nexd)=

&              sigfig(a(iscr+5+2*m+2*ki)*emev,ndigit,0)

if (xss(ki+n+nexd).lt.rmin) xss(ki+n+nexd)=0

if (ki.gt.1.and.jnt.eq.1) xss(ki+2*n+nexd)=

&              xss(ki+2*n-1+nexd)+a(iscr+5+2*m+2*(ki-1))

&              *(a(iscr+4+2*m+2*ki)-a(iscr+4+2*m+2*(ki-1)))

if (ki.gt.1.and.jnt.eq.2) xss(ki+2*n+nexd)=

&              xss(ki+2*n-1+nexd)+((a(iscr+5+2*m+2*(ki-1))

&              +a(iscr+5+2*m+2*ki))/2)*(a(iscr+4+2*m+2*ki)

&              -a(iscr+4+2*m+2*(ki-1)))

enddo

c              renormalize

renorm=1

if (xss(3*n+nexd).ne.zero) renorm=1/xss(3*n+nexd)

do ki=1,n

xss(ki+n+nexd)=sigfig(xss(ki+n+nexd)*renorm,ndigit,0)

ndig=min(9,ndigit+2)

xss(ki+2*n+nexd)=

&              sigfig(xss(ki+2*n+nexd)*renorm,ndig,0)

enddo

nexd=nexd+3*n+1

enddo

next=nexd

c

c        ***law 5...generalized evaporation spectrum

else if (lf.eq.5) then

*if sw

if (mt.eq.455) q=200.0d0

*else

if (mt.eq.455) q=200.0e0

*endif

c            call error('acelf5d','sorry. acer cannot handle lf=5.',

c     &        'you will have to patch the evaluation to use lf=1.')

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5d',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

if (m.ne.1.or.jnt.ne.2) then

xss(next)=m

do j=1,m

xss(j+next)=a(2*j+4+iscr)

xss(j+m+next)=a(2*j+5+iscr)

enddo

next=next+1+2*m

else

xss(next)=0

next=next+1

endif

do j=1,n

ein(j)=a(2*j+2*m+4+iscr)

c

c conversion only possible for simple cases

c

*if sw

if (a(2*j+2*m+5+iscr).ne.1.0d0) then

*else

if (a(2*j+2*m+5+iscr).ne.1.0e0) then

*endif

call error('acelf5d',

&          'sorry. acer cannot handle complicated lf=5.',

&          'you will have to patch the evaluation to use lf=1.')

endif

enddo

xss(next)=n

nextn=next+n

nexd=nextn+n+1

ne=n

c

c read x/g(x) pairs

c

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr

do while (nb.ne.0)

jscr=jscr+nw

call moreio(nin,0,0,a(jscr),nb,nw)

enddo

m=nint(a(iscr+4))

n=nint(a(iscr+5))

c

jnt=nint(a(iscr+5+2*m))

c

c            write(nsyso,*)  'ne =', ne

c            write(nsyso,*)  'm =', m

c            write(nsyso,*)  'n =', n

c            write(nsyso,*)  'jnt =', jnt

c

do j=1,ne

e=ein(j)

xss(next+j)=sigfig(e/emev,ndigit,0)

xss(nextn+j)=nexd-dlwnud+1

xss(nexd)=jnt

xss(nexd+1)=n

nexd=nexd+1

xss(nexd+1+2*n)=0

do ki=1,n

ep=a(iscr+4+2*m+2*ki)

if (ep.gt.e.and.q.lt.zero) then

write(nsyso,'(/'' ---warning from acelod---'',

&                  6x,''mf5 ep.gt.e with negative q''/

&                  6x,''mt='',i2,'' e='',1p,e12.4,'' ep='',e12.4/

&                  6x,''patching...'')') mt,e/emev,ep/emev

ep=e-(n-ki)*1000

a(iscr+4+2*m+2*ki)=ep

endif

xss(ki+nexd)=sigfig(a(iscr+4+2*m+2*ki)/emev,ndigit,0)

xss(ki+n+nexd)=

&              sigfig(a(iscr+5+2*m+2*ki)*emev,ndigit,0)

if (xss(ki+n+nexd).lt.rmin) xss(ki+n+nexd)=0

if (ki.gt.1.and.jnt.eq.1) xss(ki+2*n+nexd)=

&              xss(ki+2*n-1+nexd)+a(iscr+5+2*m+2*(ki-1))

&              *(a(iscr+4+2*m+2*ki)-a(iscr+4+2*m+2*(ki-1)))

if (ki.gt.1.and.jnt.eq.2) xss(ki+2*n+nexd)=

&              xss(ki+2*n-1+nexd)+((a(iscr+5+2*m+2*(ki-1))

&              +a(iscr+5+2*m+2*ki))/2)*(a(iscr+4+2*m+2*ki)

&              -a(iscr+4+2*m+2*(ki-1)))

enddo

c              renormalize

renorm=1

if (xss(3*n+nexd).ne.zero) renorm=1/xss(3*n+nexd)

do ki=1,n

xss(ki+n+nexd)=sigfig(xss(ki+n+nexd)*renorm,ndigit,0)

ndig=min(9,ndigit+2)

xss(ki+2*n+nexd)=

&              sigfig(xss(ki+2*n+nexd)*renorm,ndig,0)

c                  write(nsyso,*)  'xss(ki+nexd) =', xss(ki+nexd)

c                  write(nsyso,*)  'xss(ki+n+nexd) =', xss(ki+n+nexd)

c                  write(nsyso,*)  'xss(ki+2*n+nexd) =', xss(ki+2*n+nexd)

enddo

nexd=nexd+3*n+1

enddo

next=nexd

c

c        ***law 7...simple fission spectrum

c        ***law 9...evaporation spectrum

else if (lf.eq.7.or.lf.eq.9) then

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5d',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

if (m.ne.1.or.jnt.ne.2) then

xss(next)=m

do j=1,m

xss(j+next)=a(2*j+4+iscr)

xss(j+m+next)=a(2*j+5+iscr)

enddo

next=next+2*m+1

else

xss(next)=0

next=next+1

endif

xss(next)=n

do j=1,n

xss(j+next)=sigfig(a(2*j+2*m+4+iscr)/emev,ndigit,0)

xss(j+n+next)=sigfig(a(2*j+2*m+5+iscr)/emev,ndigit,0)

enddo

next=next+1+2*n

xss(next)=u/emeV

next=next+1

c

c        ***law 11...watt fission spectrum

else if (lf.eq.11) then

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

jnt=nint(a(iscr+7))

if (next+2*m+2*n+2.gt.max3) call error('acelf5d',

&        'insufficient space for energy distributions',' ')

if (m.ne.1.or.jnt.ne.2) then

xss(next)=m

do j=1,m

xss(j+next)=sigfig(a(2*j+4+iscr)/emev,ndigit,0)

xss(j+m+next)=sigfig(a(2*j+5+iscr)/emev,ndigit,0)

enddo

next=next+2*m+1

else

xss(next)=0

next=next+1

endif

xss(next)=n

do j=1,n

xss(j+next)=sigfig(a(2*j+2*m+4+iscr)/emev,ndigit,0)

xss(j+n+next)=sigfig(a(2*j+2*m+5+iscr)/emev,ndigit,0)

enddo

next=next+1+2*n

call tab1io(nin,0,0,a(iscr),nb,nw)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

if (next+2*m+2*n+2.gt.max3) call error('acelf5d',

&        'insufficient space for energy distributions',' ')

jnt=nint(a(iscr+7))

if (m.ne.1.or.jnt.ne.2) then

xss(next)=m

do j=1,m

xss(j+next)=sigfig(a(2*j+2*m+4+iscr)/emev,ndigit,0)

xss(j+n+next)=sigfig(a(2*j+2*m+5+iscr)/emev,ndigit,0)

enddo

next=next+1+2*m

else

xss(next)=0

next=next+1

endif

xss(next)=n

do j=1,n

xss(j+next)=sigfig(a(2*j+2*m+4+iscr)/emev,ndigit,0)

xss(j+n+next)=sigfig(a(2*j+2*m+5+iscr)*emev,ndigit,0)

enddo

next=next+1+2*n

xss(next)=sigfig(u/emev,ndigit,0)

next=next+1

c

c        ***law 12...madland-nix fission spectrum

else if (lf.eq.12) then

call tab1io(nin,0,0,a(iscr),nb,nw)

efl=a(iscr)

efh=a(iscr+1)

m=nint(a(iscr+4))

n=nint(a(iscr+5))

jnt=nint(a(iscr+7))

emin=a(iscr+6+2*m)

emax=a(iscr+6+2*m+2*n-2)

xss(next)=0

next=next+1

xss(next)=n

nextn=next+n

nexd=nextn+n+1

c           convert madland-nix to ace law=4 using the given e grid

c           and developing the e' grid adaptively.

do ie=1,n

tme=a(iscr+4+2*m+2*ie)

tmt=a(iscr+5+2*m+2*ie)

c              prime the adaptive stack

renorm=0

js=0

is=3

xs(3)=emin

ys(3)=fmn(emin,efl,efh,tmt)

xs(2)=emev

ys(2)=fmn(xs(2),efl,efh,tmt)

xs(1)=emax

ys(1)=fmn(emax,efl,efh,tmt)

c              carry out the adaptive linearization

do while (is.gt.0)

dy=0

test=1

if (is.gt.1.and.is.lt.ismax) then

xm=(xs(is-1)+xs(is))/2

ym=(ys(is-1)+ys(is))/2

yt=fmn(xm,efl,efh,tmt)

test=tol*abs(yt)+tmin

dy=abs(yt-ym)

endif

if (dy.gt.test) then

c                    not converged.

c                    add midpoint to stack and continue.

is=is+1

xs(is)=xs(is-1)

ys(is)=ys(is-1)

xs(is-1)=xm

ys(is-1)=yt

else

c                    converged.

c                    move top point in stack to temporary spectrum.

js=js+1

if (js.gt.jsmax) js=jsmax

xxs(js)=xs(is)

yys(js)=ys(is)

if (js.gt.1) renorm=renorm

&                  +(xxs(js)-xxs(js-1))*(yys(js)+yys(js-1))/2

is=is-1

endif

enddo

c              transfer spectrum to law 4

renorm=1/renorm

jnt=2

xss(next+ie)=sigfig(tme/emev,ndigit,0)

xss(nextn+ie)=nexd-dlwnud+1

xss(nexd)=jnt

nexd=nexd+1

xss(nexd)=js

xss(nexd+1+2*js)=0

do ki=1,js

xss(ki+nexd)=sigfig(xxs(ki)/emev,ndigit,0)

xss(ki+js+nexd)=sigfig(yys(ki)*renorm*emev,ndigit,0)

if (ki.gt.1.and.jnt.eq.1) xss(ki+2*js+nexd)=

&              xss(ki+2*js-1+nexd)

&              +renorm*yys(ki)*(xxs(ki)-xxs(ki-1))

if (ki.gt.1.and.jnt.eq.2) xss(ki+2*js+nexd)=

&              xss(ki+2*js-1+nexd)+renorm*(yys(ki)+yys(ki-1))

&              *(xxs(ki)-xxs(ki-1))/2

enddo

nexd=nexd+3*js+1

enddo

next=nexd

c

c        ***illegal value of lf

else

write(strng,'(''illegal lf='',i2)') lf

call error('acelf5d',strng,' ')

endif

c

c     ***end of loop over laws

c         write(nsyso,*)  'k (in acelf5d) =', k

c         write(nsyso,*)  'next =', next

enddo

call tosend(nin,0,0,a(iscr))

return

end

c

*i acer.9748

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

*i acer.9771

c

c add pointers to delayed neutron data

c

if (nnud.ne.0) then

nxs(8)=nlambdel

jxs(24)=dnu

jxs(25)=bdd

jxs(26)=ldlwnud

jxs(27)=dlwnud

endif

*d acer.9784,acer.9787

c

c print delayed-neutron relevant pointers

c

&  6x,''*                     *'',9x,''npcr'',i10/

&  6x,''*        njoy         *'',10x,''esz'',i10/

&  6x,''*                     *'',11x,''nu'',i10/

&  6x,''***********************'',10x,''mtr'',i10/

&  39x,''lqr'',i10/

*d acer.9794

c

c print delayed-neutron relevant pointers

c

&  37x,''iurpt'',i10/37x,''  dnu'',i10/38x,'' bdd'',i10/

&  37x,''dnedl'',i10/37x,'' dned'',i10/37x,''ptype'',i10/

&  38x,''ntro'',i10/

*d acer.9796,acer.9797

c

c print delayed-neutron relevant pointers

c

&  hz,aw0,tz,hd,hm,nxs(1),(nxs(i),i=3,8),

&  (jxs(i),i=1,27),(jxs(i),i=30,32),hk

*i acer.10065

if (jnu.eq.3) write(nsyso,

&           '('' delayed nu''/'' --------''/)')

*i acer.10066

if (jnu.eq.3) then

l=dnu

j=nint(xss(l))

endif

*d acer.10106

if (nnud.eq.0.and.jnu.eq.1.and.kf.lt.0) idone=0

if (nnud.ne.0.and.jnu.ne.3.and.kf.lt.0) idone=0

*i acer.10203

common/ace1/tempd,err,matd,nbina,nbinp,negn,iprint,iopt,ndigit

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

common/astore/a(80000)

*if sw

data tshake/1.d8/

*else

data tshake/1.e8/

*endif

*d acer.10211

nr1=nr

if (nnud.ne.0) then

c

c delayed neutron data present

c

nr1=nr+1

endif

do n=1,nr1

c

c

*i acer.10213

if (n.eq.nr1.and.nnud.ne.0) then

title(1)='del. fiss.'

mtrn=455

endif

*i acer.10224

if (n.eq.nr1.and.nnud.ne.0) then

l=nint(xss(ldlwnud)+dlwnud-1)

c         write(nsyso,*)  'l =', l

c         write(nsyso,*)  'xss(l) =', xss(l)

loc(1)=l

do while (nint(xss(l)).ne.0)

l=nint(xss(l))+dlwnud-1

nlaw=nlaw+1

loc(nlaw)=l

enddo

else

*i acer.10231

endif

*i acer.10374

if (n.eq.nr1.and.nnud.ne.0) then

delay=sigfig(a(ilambdel+m-1)/tshake,ndigit,0)

write(nsyso,'(12x,''decay constant = '',1p,e14.6,

&            '' (per shake)'')')delay

endif

*d acer.10390

if (n.eq.nr1.and.nnud.ne.0) then

loci=nint(xss(ie+ne+l)+dlwnud-1)

else

loci=nint(xss(ie+ne+l)+dlw)

endif

*i acer.11592

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

*i acer.11688

common/nud/nnud,nlambdel,nnfd,dlwnud,ldlwnud,ilambdel,bdd,dnu

integer bdd,dlwnud,dnu

*i acer.12302

c

c     ***delayed fission neutron energy distributions

if (nnfd.ne.0) then

c

c        ***nud block

l=dnu

if (nout.ne.1) lnu=nint(xss(l))

if (nout.eq.1) lnu=iss(l)

call typen(l,nout,1)

l=l+1

if (lnu.ne.2) then

if (nout.ne.1) nc=nint(xss(l))

if (nout.eq.1) nc=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,nc

call typen(l,nout,2)

l=l+1

enddo

else

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.ne.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

endif

c

c        ***bdd block

l=bdd

do while (l.lt.ldlwnud)

call typen(l,nout,2)

l=l+1

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

enddo

c

c        ***ldlwnud block

l=ldlwnud

do i=1,nnfd

call typen(l,nout,1)

l=l+1

enddo

c

c        ***dlwnud block

l=dlwnud

do i=1,nnfd

c

c           ***loop over laws

if (nout.ne.1) lnw=nint(xss(l))

if (nout.eq.1) lnw=iss(l)

call typen(l,nout,1)

l=l+1

if (nout.ne.1) law=nint(xss(l))

if (nout.eq.1) law=iss(l)

call typen(l,nout,1)

l=l+1

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

c

c              ***law 1

if (law.eq.1) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

if (nout.ne.1) net=nint(xss(l))

if (nout.eq.1) net=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

do k=1,net

call typen(l,nout,2)

l=l+1

enddo

enddo

c

c              ***law 3

else if (law.eq.3) then

call typen(l,nout,2)

l=l+1

call typen(l,nout,2)

l=l+1

c

c              ***law 4

else if (law.eq.4) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

if (nout.ne.1) np=nint(xss(l))

if (nout.eq.1) np=iss(l)

call typen(l,nout,1)

l=l+1

n=3*np

do k=1,n

call typen(l,nout,2)

l=l+1

enddo

enddo

c

c              ***law 5

else if (law.eq.5) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

if (nout.ne.1) net=nint(xss(l))

if (nout.eq.1) net=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,net

call typen(l,nout,2)

l=l+1

enddo

c

c              ***law 7 or law 9

else if (law.eq.7.or.law.eq.9) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

call typen(l,nout,2)

l=l+1

c

c              ***law 11

else if (law.eq.11) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

n=2*ne

do j=1,n

call typen(l,nout,2)

l=l+1

enddo

call typen(l,nout,2)

l=l+1

c

c              ***law 44

else if (law.eq.44) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

if (nout.ne.1) np=nint(xss(l))

if (nout.eq.1) np=iss(l)

call typen(l,nout,1)

l=l+1

n=5*np

do k=1,n

call typen(l,nout,2)

l=l+1

enddo

enddo

c

c              ***law 61

else if (law.eq.61) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.ne.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

if (nout.ne.1) np=nint(xss(l))

if (nout.eq.1) np=iss(l)

call typen(l,nout,1)

l=l+1

n=3*np

do k=1,n

call typen(l,nout,2)

l=l+1

enddo

do k=1,np

call typen(l,nout,1)

l=l+1

enddo

do k=1,np

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nmu=nint(xss(l))

if (nout.eq.1) nmu=iss(l)

call typen(l,nout,1)

l=l+1

nw=3*nmu

do kk=1,nw

call typen(l,nout,2)

l=l+1

enddo

enddo

enddo

c

c              ***law 66

else if (law.eq.66) then

call typen(l,nout,1)

l=l+1

call typen(l,nout,2)

l=l+1

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nn=nint(xss(l))

if (nout.eq.1) nn=iss(l)

n=3*nn

call typen(l,nout,1)

l=l+1

do k=1,n

call typen(l,nout,2)

l=l+1

enddo

c

c              ***law 67

else if (law.eq.67) then

if (nout.ne.1) nr=nint(xss(l))

if (nout.eq.1) nr=iss(l)

call typen(l,nout,1)

l=l+1

if (nr.gt.0) then

n=2*nr

do j=1,n

call typen(l,nout,1)

l=l+1

enddo

endif

if (nout.ne.1) ne=nint(xss(l))

if (nout.eq.1) ne=iss(l)

call typen(l,nout,1)

l=l+1

do j=1,ne

call typen(l,nout,2)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

enddo

do j=1,ne

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nmu=nint(xss(l))

if (nout.eq.1) nmu=iss(l)

call typen(l,nout,1)

l=l+1

do k=1,nmu

call typen(l,nout,2)

l=l+1

enddo

do k=1,nmu

call typen(l,nout,1)

l=l+1

enddo

do k=1,nmu

call typen(l,nout,1)

l=l+1

if (nout.ne.1) nep=nint(xss(l))

if (nout.eq.1) nep=iss(l)

call typen(l,nout,1)

l=l+1

nn=3*nep

do n=1,nn

call typen(l,nout,2)

l=l+1

enddo

enddo

enddo

endif

enddo

endif

c

*/

*ident nrg_a52

*/ acer -- 14feb2002 A. Hogenbirk (NRG)

*/ -----------------------------------------------

*/          Allow presence of MF1,MT455 data

*/          while energy distributions in MF5 are lacking.

*/          However, print relevant warning message!

*/ -----------------------------------------------

*/

*d up57.10

common/ace9/mt16,mt455

*i up57.12

mt455=0

*i up57.14

if (mfd.eq.5.and.mtd.eq.455) mt455=1

*d up57.18

common/ace9/mt16,mt455

*d nrg_a50.9

&     (mf.eq.5.and.mt.gt.900)) then

*d nrg_a50.81

if (nnud.gt.0.and.mt455.eq.0) write(nsyso,

&  '(/''   A delayed nubar section was found in MF1, but''/

&     ''   no delayed neutron spectra were found in MF5:''/

&     ''   Only the total spectrum will be output to the''

&     '' ace library'')')

if (nnud.gt.0.and.mt455.eq.1) then

write(nsyso,'(/''  adding delayed neutron data'')')

*/

*/ Included in upn_ADS changed to ads03.33

*/ *i up57.102

*/      common/ace9/mt16,mt455

*i acer.11688

common/ace9/mt16,mt455

*/

*d nrg_a50.880

if (nnfd.gt.0.and.mt455.eq.1) then

c

c only print delayed information if spectrum is given on evaluation

*/

*/ Included in upn_ADS changed to ads03.33

*/ *i up57.92

*/       common/ace9/mt16,mt455

*i acer.9753

common/ace9/mt16,mt455

*/

*i nrg_a50.818

if (nnud.gt.0.and.jnu.eq.2.and.mt455.eq.0) idone=1

c

c no delayed spectrum on evaluation!

c

*i nrg_a50.823

common/ace9/mt16,mt455

*d nrg_a50.831

if (nnud.gt.0.and.mt455.eq.1) then

*d nrg_a50.841

if (n.eq.nr1.and.nnud.gt.0.and.mt455.eq.1) then

*d nrg_a50.846

if (n.eq.nr1.and.nnud.gt.0.and.mt455.eq.1) then

*d nrg_a50.860

if (n.eq.nr1.and.nnud.gt.0.and.mt455.eq.1) then

*d nrg_a50.866

if (n.eq.nr1.and.nnud.gt.0.and.mt455.eq.1) then

*/

*ident nrg_a57

*/ acer -- 07mar2002 A. Hogenbirk (NRG)

*/ -----------------------------------------------

*/          do not output delayed neutron information at all

*/          when energy distributions are lacking...

*/ -----------------------------------------------

*/

*d nrg_a50.779

if (nnud.gt.0.and.mt455.eq.1) then

*/

*ident nrg_re15

*/ reconr -- 25feb2005 A. Hogenbirk (NRG)

*/ -----------------------------------------------

*/  Add forgotten initialisation of zero

*/ -----------------------------------------------

*/

*i reconr.853

zero=0

*i reconr.937

zero=0

*/

## C.7 upn_Sublet

REM upn_Sublet   : upki (included in upn_Hogenbirk)

*/ Updates Sublet

*/

*/  J.C. Sublet, Feb. 2005

*/  increase the allowed number of legendre terms in h6ddx

*/  to handle the new ENDF/B-VII (Mo95) evaluation.

*/

*ident upki

*d up15.9

dimension cnow(*),p(65)

*d up30.10

*i heatr.3298

data nlmax/65/

## C.8 upn_ADS

REM upn_ADS      :

REM                  - Include: ads01, ads02, ads03

REM                  - Do not include:

REM                1) upiaea1, upijs57, upijs59, upijs61, upijs62, upijs63, upijs64

REM                   upiaea2 upiaea3, upfendl1, upfndl2, upfndl3, upfndl4,

REM                   upfndl5, upfndl6: included in upn_Trkov

REM                2) wlup2: included in upn_Aldama

REM                3) up3_thermr, up1_leapr, up2_leapr, up3_leapr, up4_leapr,

REM                   up5_leapr, up_acer : included in upn_Mattes

REM                4) upshim: included in upn_Shimizu

REM                5) upcad: included in upn_CAD

*/

*ident ads01

*/ matxsr - D. L. Aldama, NDS/IAEA Consultant, July 2005

*/ Need more space  (for processing ORNL 421 energy group structure)

*/  subroutine vector

*d up88.21

dimension b(30000)

*d up88.23

maxb=30000

*ident ads02

*/ matxsr - D. L. Aldama, NDS/IAEA Consultant, July 2005

*/ Remove a problem in case of multi-temperature matxs files processing.

*/ Scratch tapes iref and nscr should be simultaneously forwarded.

*/ The problem seems to affect only multi-temperature runs, if the mf=6

*/ of gendf tape was not ordered by mt numbers.

*/

*i matxsr.1870

if (iref.ne.0) call contio(iref,0,0,b(1),nb,nw)

*d matxsr.1878

if (iskip.eq.0) then

if (iref.ne.0) call tosend(iref,0,0,b(1))

call tosend(nscr,0,0,b(1))

endif

*/

*ident ads03

*/ acer - D. L. Aldama, NDS/IAEA Consultant, July 2005

*/ need more storage for processing jeff-3.1 U-238

*/ ADS library

*/

*d up57.76

max3=4000000

*d up57.78

common/xsst/xss(4000000),n3

*d up57.80

common/xsst/xss(4000000),n3

*d up57.82

common/xsst/xss(4000000),n3

*d up57.84

common/xsst/xss(4000000),n3

*d up57.86

common/xsst/xss(4000000),n3

*d up57.88

common/xsst/xss(4000000),n3

*d up57.90

common/xsst/xss(4000000),n3

*d up57.92

common/xsst/xss(4000000),n3

*d up57.94

common/xsst/xss(4000000),n3

*d up57.96

common/xsst/xss(4000000),n3

*d up57.98

common/xsst/xss(4000000),n3

*d up57.100

common/xsst/xss(4000000),n3

*d up57.102

common/xsst/xss(4000000),n3

*d up57.104

common/xsst/xss(4000000),n3

*d up57.106

common/xsst/xss(4000000),n3

*d up57.108

common/xsst/xss(4000000),n3

*d up57.110

common/xsst/xss(4000000),n3

*d up57.112

common/xsst/xss(4000000),n3

*d up57.114

common/xsst/xss(4000000),n3

*d up57.116

common/xsst/xss(4000000),n3

*d up57.118

common/xsst/xss(4000000),n3

*d up57.120

common/xsst/xss(4000000),n3

*d up57.122

common/xsst/xss(4000000),n3

*d up57.124

common/xsst/xss(4000000),n3

*d up57.126

common/xsst/xss(4000000),n3

*d up57.128

common/xsst/xss(4000000),n3

*d up57.130

common/xsst/xss(4000000),n3

*d up57.132

common/xsst/xss(4000000),n3

*d up57.134

common/xsst/xss(4000000),n3

*d up57.136

common/xsst/xss(4000000),n3

*d up57.138

common/xsst/xss(4000000),n3

*d up57.140

common/xsst/xss(4000000),n3

*d up57.142

common/xsst/xss(4000000),n3

*d up70.95

common/xsst/xss(4000000),n3

*d up57.144

common/xsst/xss(4000000),n3

*d up70.222

common/xsst/xss(4000000),n3

*d up57.146

common/xsst/xss(4000000),n3

*d up57.148

common/xsst/xss(4000000),n3

*d up57.150

common/xsst/xss(4000000),n3

*/

## C.9 upn_CAD

REM upn_CAD      : upcad (included in ADS)

*/

*ident upcad

*/ groupr -- 11oct2002

*/   add the ecco33, ecco1968, tripoli315, xmas172 and Vitamin-J

*/   group structures with 7 significant decimal digits. those

*/   group structures are used in Europe for fast breeder and

*/   thermal reactor neutronics calculations. for compatibility

*/   with Calendf and Apollo

*b groupr.132

c     *     18           xmas NEA-LANL

c     *     All new additional group structure with 7 significant

c     *     decimal digits compatible with CALENDF

c     *     19           ecco  33-group structure

c     *     20           ecco 1968-group structure

c     *     21           tripoli 315-group structure

c     *     22           xmas LWPC 172-group structure

c     *     23           vit-J LWPC 175-group structure

*b groupr.1297

c        19      ecco  33-group structure

c        20      ecco 1968-group structure

c        21      tripoli 315-group structure

c        22      xmas LWPC 172-group structure

c        23      vit-J LWPC 175-group structure

*b groupr.1312

dimension eg19(34)

dimension eg20(1969)

dimension eg20a(95),eg20b(95),eg20c(95),eg20d(95),

*          eg20e(95),eg20f(95),eg20g(95),eg20h(95),

*          eg20i(95),eg20j(95),eg20k(95),eg20l(95),

*          eg20m(95),eg20n(95),eg20o(95),eg20p(95),

*          eg20q(95),eg20r(95),eg20s(95),eg20t(95),

*          eg20u(69)

dimension eg21(316)

dimension eg21a(95),eg21b(95),eg21c(95),eg21d(31)

dimension eg22(173)

dimension eg22a(95),eg22b(78)

dimension eg23(176)

dimension eg23a(95),eg23b(81)

equivalence (eg20a(1),eg20(1)),(eg20b(1),eg20(96)),

*            (eg20c(1),eg20(191)),(eg20d(1),eg20(286)),

*            (eg20e(1),eg20(381)),(eg20f(1),eg20(476)),

*            (eg20g(1),eg20(571)),(eg20h(1),eg20(666)),

*            (eg20i(1),eg20(761)),(eg20j(1),eg20(856)),

*            (eg20k(1),eg20(951)),(eg20l(1),eg20(1046)),

*            (eg20m(1),eg20(1141)),(eg20n(1),eg20(1236)),

*            (eg20o(1),eg20(1331)),(eg20p(1),eg20(1426)),

*            (eg20q(1),eg20(1521)),(eg20r(1),eg20(1616)),

*            (eg20s(1),eg20(1711)),(eg20t(1),eg20(1806)),

*            (eg20u(1),eg20(1901))

equivalence (eg21a(1),eg21(1)),(eg21b(1),eg21(96)),

*            (eg21c(1),eg21(191)),(eg21d(1),eg21(286))

equivalence (eg22a(1),eg22(1)),(eg22b(1),eg22(96))

equivalence (eg23a(1),eg23(1)),(eg23b(1),eg23(96))

*b groupr.1470

data eg19/

&1.000010d-05,1.000000d-01,5.400000d-01,4.000000d+00,8.315287d+00,

&1.370959d+01,2.260329d+01,4.016900d+01,6.790405d+01,9.166088d+01,

&1.486254d+02,3.043248d+02,4.539993d+02,7.485183d+02,1.234098d+03,

&2.034684d+03,3.354626d+03,5.530844d+03,9.118820d+03,1.503439d+04,

&2.478752d+04,4.086771d+04,6.737947d+04,1.110900d+05,1.831564d+05,

&3.019738d+05,4.978707d+05,8.208500d+05,1.353353d+06,2.231302d+06,

&3.678794d+06,6.065307d+06,1.000000d+07,1.964033d+07/

data eg20a/

&1.000010d-05,3.000000d-03,5.000000d-03,6.900000d-03,1.000000d-02,

&1.500000d-02,2.000000d-02,2.500000d-02,3.000000d-02,3.500000d-02,

&4.200000d-02,5.000000d-02,5.800000d-02,6.700000d-02,7.700000d-02,

&8.000000d-02,9.500000d-02,1.000000d-01,1.150000d-01,1.340000d-01,

&1.400000d-01,1.463700d-01,1.530300d-01,1.600000d-01,1.697100d-01,

&1.800000d-01,1.890000d-01,1.988100d-01,2.091400d-01,2.200000d-01,

&2.335800d-01,2.480000d-01,2.635100d-01,2.800000d-01,3.000000d-01,

&3.145000d-01,3.200000d-01,3.346600d-01,3.500000d-01,3.699300d-01,

&3.910000d-01,4.000000d-01,4.139900d-01,4.330000d-01,4.496800d-01,

&4.670100d-01,4.850000d-01,5.000000d-01,5.196200d-01,5.315800d-01,

&5.400000d-01,5.669600d-01,5.952800d-01,6.250000d-01,6.531500d-01,

&6.825600d-01,7.050000d-01,7.415500d-01,7.800000d-01,7.900000d-01,

&8.194500d-01,8.500000d-01,8.600000d-01,8.764250d-01,9.100000d-01,

&9.300000d-01,9.500000d-01,9.720000d-01,9.860000d-01,9.960000d-01,

&1.020000d+00,1.035000d+00,1.045000d+00,1.071000d+00,1.080000d+00,

&1.097000d+00,1.110000d+00,1.123000d+00,1.150000d+00,1.170000d+00,

&1.202060d+00,1.235000d+00,1.267080d+00,1.300000d+00,1.337500d+00,

&1.370000d+00,1.404560d+00,1.440000d+00,1.475000d+00,1.500000d+00,

&1.544340d+00,1.590000d+00,1.629510d+00,1.670000d+00,1.711970d+00/

data eg20b/

&1.755000d+00,1.797000d+00,1.840000d+00,1.855390d+00,1.884460d+00,

&1.930000d+00,1.974490d+00,2.020000d+00,2.059610d+00,2.100000d+00,

&2.130000d+00,2.185310d+00,2.242050d+00,2.300270d+00,2.360000d+00,

&2.382370d+00,2.421710d+00,2.485030d+00,2.550000d+00,2.600000d+00,

&2.659320d+00,2.720000d+00,2.767920d+00,2.837990d+00,2.909830d+00,

&2.983490d+00,3.059020d+00,3.137330d+00,3.217630d+00,3.300000d+00,

&3.380750d+00,3.466330d+00,3.554080d+00,3.644050d+00,3.736300d+00,

&3.830880d+00,3.927860d+00,4.000000d+00,4.129250d+00,4.233782d+00,

&4.340961d+00,4.450853d+00,4.563526d+00,4.679053d+00,4.797503d+00,

&4.918953d+00,5.043477d+00,5.085681d+00,5.128239d+00,5.171153d+00,

&5.214426d+00,5.258061d+00,5.302061d+00,5.346430d+00,5.391169d+00,

&5.436284d+00,5.481775d+00,5.527647d+00,5.573904d+00,5.620547d+00,

&5.667581d+00,5.715008d+00,5.762832d+00,5.811056d+00,5.859684d+00,

&5.908719d+00,5.958164d+00,6.008022d+00,6.058298d+00,6.108995d+00,

&6.160116d+00,6.211665d+00,6.263645d+00,6.316060d+00,6.368914d+00,

&6.422210d+00,6.475952d+00,6.530144d+00,6.584789d+00,6.639892d+00,

&6.695455d+00,6.751484d+00,6.807981d+00,6.864952d+00,6.922399d+00,

&6.980326d+00,7.038739d+00,7.097640d+00,7.157034d+00,7.216925d+00,

&7.277317d+00,7.338215d+00,7.399622d+00,7.461544d+00,7.523983d+00/

data eg20c/

&7.586945d+00,7.650434d+00,7.714454d+00,7.779009d+00,7.844105d+00,

&7.909746d+00,7.975936d+00,8.042680d+00,8.109982d+00,8.177848d+00,

&8.246281d+00,8.315287d+00,8.384871d+00,8.455037d+00,8.525790d+00,

&8.597135d+00,8.669077d+00,8.741621d+00,8.814772d+00,8.888536d+00,

&8.962916d+00,9.037919d+00,9.113550d+00,9.189814d+00,9.266715d+00,

&9.344261d+00,9.422455d+00,9.501303d+00,9.580812d+00,9.660985d+00,

&9.741830d+00,9.823351d+00,9.905554d+00,9.988446d+00,1.007203d+01,

&1.015631d+01,1.024130d+01,1.032701d+01,1.041342d+01,1.050056d+01,

&1.058843d+01,1.067704d+01,1.076639d+01,1.085648d+01,1.094733d+01,

&1.103894d+01,1.113132d+01,1.122446d+01,1.131839d+01,1.141311d+01,

&1.150861d+01,1.160492d+01,1.170203d+01,1.179995d+01,1.189870d+01,

&1.199827d+01,1.209867d+01,1.219991d+01,1.230201d+01,1.240495d+01,

&1.250876d+01,1.261343d+01,1.271898d+01,1.282542d+01,1.293274d+01,

&1.304097d+01,1.315010d+01,1.326014d+01,1.337110d+01,1.348299d+01,

&1.359582d+01,1.370959d+01,1.382431d+01,1.394000d+01,1.405665d+01,

&1.417428d+01,1.429289d+01,1.441250d+01,1.453310d+01,1.465472d+01,

&1.477735d+01,1.490101d+01,1.502570d+01,1.515144d+01,1.527823d+01,

&1.540608d+01,1.553500d+01,1.566500d+01,1.579609d+01,1.592827d+01,

&1.606156d+01,1.619597d+01,1.633150d+01,1.646816d+01,1.660597d+01/

data eg20d/

&1.674493d+01,1.688506d+01,1.702635d+01,1.716883d+01,1.731250d+01,

&1.745738d+01,1.760346d+01,1.775077d+01,1.789931d+01,1.804910d+01,

&1.820013d+01,1.835244d+01,1.850601d+01,1.866087d+01,1.881703d+01,

&1.897449d+01,1.913328d+01,1.929339d+01,1.945484d+01,1.961764d+01,

&1.978180d+01,1.994734d+01,2.011426d+01,2.028258d+01,2.045231d+01,

&2.062345d+01,2.079603d+01,2.097006d+01,2.114554d+01,2.132249d+01,

&2.150092d+01,2.168084d+01,2.186227d+01,2.204522d+01,2.222969d+01,

&2.241572d+01,2.260329d+01,2.279244d+01,2.298317d+01,2.317550d+01,

&2.336944d+01,2.356499d+01,2.376219d+01,2.396104d+01,2.416154d+01,

&2.436373d+01,2.456761d+01,2.477320d+01,2.498050d+01,2.518954d+01,

&2.540033d+01,2.561289d+01,2.582722d+01,2.604335d+01,2.626128d+01,

&2.648104d+01,2.670264d+01,2.692609d+01,2.715141d+01,2.737862d+01,

&2.760773d+01,2.783875d+01,2.807171d+01,2.830662d+01,2.854349d+01,

&2.878235d+01,2.902320d+01,2.926607d+01,2.951098d+01,2.975793d+01,

&3.000695d+01,3.025805d+01,3.051126d+01,3.076658d+01,3.102404d+01,

&3.128365d+01,3.154544d+01,3.180942d+01,3.207560d+01,3.234401d+01,

&3.261467d+01,3.288760d+01,3.316281d+01,3.344032d+01,3.372015d+01,

&3.400233d+01,3.428686d+01,3.457378d+01,3.486310d+01,3.515484d+01,

&3.544902d+01,3.574566d+01,3.604479d+01,3.634642d+01,3.665057d+01/

data eg20e/

&3.695727d+01,3.726653d+01,3.757838d+01,3.789285d+01,3.820994d+01,

&3.852969d+01,3.885211d+01,3.917723d+01,3.950507d+01,3.983565d+01,

&4.016900d+01,4.050514d+01,4.084410d+01,4.118589d+01,4.153054d+01,

&4.187807d+01,4.222851d+01,4.258189d+01,4.293822d+01,4.329753d+01,

&4.365985d+01,4.402521d+01,4.439361d+01,4.476511d+01,4.513971d+01,

&4.551744d+01,4.589834d+01,4.628243d+01,4.666972d+01,4.706026d+01,

&4.745407d+01,4.785117d+01,4.825160d+01,4.865538d+01,4.906253d+01,

&4.947309d+01,4.988709d+01,5.030456d+01,5.072551d+01,5.114999d+01,

&5.157802d+01,5.200963d+01,5.244486d+01,5.288373d+01,5.332626d+01,

&5.377251d+01,5.422248d+01,5.467623d+01,5.513376d+01,5.559513d+01,

&5.606036d+01,5.652948d+01,5.700253d+01,5.747954d+01,5.796053d+01,

&5.844556d+01,5.893464d+01,5.942781d+01,5.992511d+01,6.042657d+01,

&6.093223d+01,6.144212d+01,6.195628d+01,6.247474d+01,6.299754d+01,

&6.352471d+01,6.405630d+01,6.459233d+01,6.513285d+01,6.567789d+01,

&6.622749d+01,6.678169d+01,6.734053d+01,6.790405d+01,6.847228d+01,

&6.904527d+01,6.962305d+01,7.020566d+01,7.079316d+01,7.138556d+01,

&7.198293d+01,7.258529d+01,7.319270d+01,7.380518d+01,7.442280d+01,

&7.504558d+01,7.567357d+01,7.630682d+01,7.694537d+01,7.758926d+01,

&7.823854d+01,7.889325d+01,7.955344d+01,8.021915d+01,8.089044d+01/

data eg20f/

&8.156734d+01,8.224991d+01,8.293819d+01,8.363223d+01,8.433208d+01,

&8.503778d+01,8.574939d+01,8.646695d+01,8.719052d+01,8.792015d+01,

&8.865588d+01,8.939776d+01,9.014586d+01,9.090021d+01,9.166088d+01,

&9.242791d+01,9.320136d+01,9.398128d+01,9.476773d+01,9.556076d+01,

&9.636043d+01,9.716679d+01,9.797990d+01,9.879981d+01,9.962658d+01,

&1.004603d+02,1.013009d+02,1.021486d+02,1.030034d+02,1.038654d+02,

&1.047345d+02,1.056110d+02,1.064947d+02,1.073859d+02,1.082845d+02,

&1.091907d+02,1.101044d+02,1.110258d+02,1.119548d+02,1.128917d+02,

&1.138364d+02,1.147890d+02,1.157496d+02,1.167182d+02,1.176949d+02,

&1.186798d+02,1.196729d+02,1.206744d+02,1.216842d+02,1.227024d+02,

&1.237292d+02,1.247646d+02,1.258087d+02,1.268615d+02,1.279231d+02,

&1.289935d+02,1.300730d+02,1.311615d+02,1.322590d+02,1.333658d+02,

&1.344818d+02,1.356072d+02,1.367420d+02,1.378862d+02,1.390401d+02,

&1.402036d+02,1.413768d+02,1.425599d+02,1.437529d+02,1.449558d+02,

&1.461688d+02,1.473920d+02,1.486254d+02,1.498691d+02,1.511232d+02,

&1.523879d+02,1.536631d+02,1.549489d+02,1.562456d+02,1.575531d+02,

&1.588715d+02,1.602010d+02,1.615415d+02,1.628933d+02,1.642565d+02,

&1.656310d+02,1.670170d+02,1.684146d+02,1.698239d+02,1.712451d+02,

&1.726781d+02,1.741231d+02,1.755802d+02,1.770494d+02,1.785310d+02/

data eg20g/

&1.800250d+02,1.815315d+02,1.830505d+02,1.845823d+02,1.861269d+02,

&1.876845d+02,1.892551d+02,1.908388d+02,1.924358d+02,1.940461d+02,

&1.956699d+02,1.973073d+02,1.989584d+02,2.006233d+02,2.023021d+02,

&2.039950d+02,2.057021d+02,2.074234d+02,2.091592d+02,2.109095d+02,

&2.126744d+02,2.144541d+02,2.162487d+02,2.180583d+02,2.198830d+02,

&2.217230d+02,2.235784d+02,2.254494d+02,2.273360d+02,2.292384d+02,

&2.311567d+02,2.330910d+02,2.350416d+02,2.370084d+02,2.389917d+02,

&2.409917d+02,2.430083d+02,2.450418d+02,2.470924d+02,2.491601d+02,

&2.512451d+02,2.533476d+02,2.554676d+02,2.576054d+02,2.597611d+02,

&2.619348d+02,2.641267d+02,2.663370d+02,2.685657d+02,2.708131d+02,

&2.730793d+02,2.753645d+02,2.776688d+02,2.799924d+02,2.823354d+02,

&2.846980d+02,2.870804d+02,2.894827d+02,2.919052d+02,2.943479d+02,

&2.968110d+02,2.992948d+02,3.017993d+02,3.043248d+02,3.068715d+02,

&3.094394d+02,3.120288d+02,3.146399d+02,3.172729d+02,3.199279d+02,

&3.226051d+02,3.253047d+02,3.280269d+02,3.307719d+02,3.335398d+02,

&3.363309d+02,3.391454d+02,3.419834d+02,3.448452d+02,3.477309d+02,

&3.506408d+02,3.535750d+02,3.565338d+02,3.595173d+02,3.625258d+02,

&3.655595d+02,3.686185d+02,3.717032d+02,3.748137d+02,3.779502d+02,

&3.811129d+02,3.843021d+02,3.875180d+02,3.907608d+02,3.940308d+02/

data eg20h/

&3.973281d+02,4.006530d+02,4.040057d+02,4.073865d+02,4.107955d+02,

&4.142332d+02,4.176995d+02,4.211949d+02,4.247195d+02,4.282736d+02,

&4.318575d+02,4.354713d+02,4.391154d+02,4.427900d+02,4.464953d+02,

&4.502317d+02,4.539993d+02,4.577984d+02,4.616294d+02,4.654923d+02,

&4.693877d+02,4.733156d+02,4.772763d+02,4.812703d+02,4.852976d+02,

&4.893587d+02,4.934537d+02,4.975830d+02,5.017468d+02,5.059455d+02,

&5.101793d+02,5.144486d+02,5.187536d+02,5.230946d+02,5.274719d+02,

&5.318859d+02,5.363368d+02,5.408249d+02,5.453506d+02,5.499142d+02,

&5.545160d+02,5.591563d+02,5.638354d+02,5.685536d+02,5.733114d+02,

&5.781089d+02,5.829466d+02,5.878248d+02,5.927438d+02,5.977040d+02,

&6.027057d+02,6.077492d+02,6.128350d+02,6.179633d+02,6.231345d+02,

&6.283489d+02,6.336071d+02,6.389092d+02,6.442557d+02,6.496469d+02,

&6.550832d+02,6.605651d+02,6.660928d+02,6.716668d+02,6.772874d+02,

&6.829550d+02,6.886701d+02,6.944330d+02,7.002441d+02,7.061038d+02,

&7.120126d+02,7.179709d+02,7.239790d+02,7.300373d+02,7.361464d+02,

&7.423066d+02,7.485183d+02,7.547820d+02,7.610981d+02,7.674671d+02,

&7.738894d+02,7.803654d+02,7.868957d+02,7.934805d+02,8.001205d+02,

&8.068160d+02,8.135676d+02,8.203756d+02,8.272407d+02,8.341631d+02,

&8.411435d+02,8.481824d+02,8.552801d+02,8.624372d+02,8.696542d+02/

data eg20i/

&8.769316d+02,8.842699d+02,8.916696d+02,8.991312d+02,9.066553d+02,

&9.142423d+02,9.218928d+02,9.296074d+02,9.373865d+02,9.452307d+02,

&9.531405d+02,9.611165d+02,9.691593d+02,9.772694d+02,9.854473d+02,

&9.936937d+02,1.002009d+03,1.010394d+03,1.018849d+03,1.027375d+03,

&1.035972d+03,1.044641d+03,1.053383d+03,1.062198d+03,1.071087d+03,

&1.080050d+03,1.089088d+03,1.098201d+03,1.107391d+03,1.116658d+03,

&1.126002d+03,1.135425d+03,1.144926d+03,1.154507d+03,1.164168d+03,

&1.173910d+03,1.183734d+03,1.193639d+03,1.203628d+03,1.213700d+03,

&1.223857d+03,1.234098d+03,1.244425d+03,1.254839d+03,1.265339d+03,

&1.275928d+03,1.286605d+03,1.297372d+03,1.308228d+03,1.319176d+03,

&1.330215d+03,1.341346d+03,1.352571d+03,1.363889d+03,1.375303d+03,

&1.386811d+03,1.398416d+03,1.410118d+03,1.421919d+03,1.433817d+03,

&1.445816d+03,1.457915d+03,1.470115d+03,1.482417d+03,1.494822d+03,

&1.507331d+03,1.519944d+03,1.532663d+03,1.545489d+03,1.558422d+03,

&1.571463d+03,1.584613d+03,1.597874d+03,1.611245d+03,1.624728d+03,

&1.638324d+03,1.652034d+03,1.665858d+03,1.679798d+03,1.693855d+03,

&1.708030d+03,1.722323d+03,1.736735d+03,1.751268d+03,1.765923d+03,

&1.780701d+03,1.795602d+03,1.810628d+03,1.825780d+03,1.841058d+03,

&1.856464d+03,1.871999d+03,1.887665d+03,1.903461d+03,1.919389d+03/

data eg20j/

&1.935451d+03,1.951647d+03,1.967979d+03,1.984447d+03,2.001053d+03,

&2.017798d+03,2.034684d+03,2.051710d+03,2.068879d+03,2.086192d+03,

&2.103650d+03,2.121253d+03,2.139004d+03,2.156904d+03,2.174953d+03,

&2.193153d+03,2.211506d+03,2.230012d+03,2.248673d+03,2.267490d+03,

&2.286465d+03,2.305599d+03,2.324892d+03,2.344347d+03,2.363965d+03,

&2.383747d+03,2.403695d+03,2.423809d+03,2.444092d+03,2.464545d+03,

&2.485168d+03,2.505965d+03,2.526935d+03,2.548081d+03,2.569403d+03,

&2.590904d+03,2.612586d+03,2.634448d+03,2.656494d+03,2.678723d+03,

&2.701139d+03,2.723743d+03,2.746536d+03,2.769519d+03,2.792695d+03,

&2.816065d+03,2.839630d+03,2.863392d+03,2.887354d+03,2.911515d+03,

&2.935879d+03,2.960447d+03,2.985221d+03,3.010202d+03,3.035391d+03,

&3.060792d+03,3.086405d+03,3.112233d+03,3.138276d+03,3.164538d+03,

&3.191019d+03,3.217722d+03,3.244649d+03,3.271800d+03,3.299179d+03,

&3.326787d+03,3.354626d+03,3.382698d+03,3.411005d+03,3.439549d+03,

&3.468332d+03,3.497355d+03,3.526622d+03,3.556133d+03,3.585891d+03,

&3.615898d+03,3.646157d+03,3.676668d+03,3.707435d+03,3.738460d+03,

&3.769744d+03,3.801290d+03,3.833099d+03,3.865175d+03,3.897520d+03,

&3.930135d+03,3.963023d+03,3.996186d+03,4.029627d+03,4.063347d+03,

&4.097350d+03,4.131637d+03,4.166211d+03,4.201075d+03,4.236230d+03/

data eg20k/

&4.271679d+03,4.307425d+03,4.343471d+03,4.379817d+03,4.416468d+03,

&4.453426d+03,4.490693d+03,4.528272d+03,4.566165d+03,4.604375d+03,

&4.642906d+03,4.681758d+03,4.720936d+03,4.760441d+03,4.800277d+03,

&4.840447d+03,4.880952d+03,4.921797d+03,4.962983d+03,5.004514d+03,

&5.046393d+03,5.088622d+03,5.131204d+03,5.174143d+03,5.217441d+03,

&5.261101d+03,5.305127d+03,5.349521d+03,5.394287d+03,5.439427d+03,

&5.484945d+03,5.530844d+03,5.577127d+03,5.623797d+03,5.670858d+03,

&5.718312d+03,5.766164d+03,5.814416d+03,5.863072d+03,5.912135d+03,

&5.961609d+03,6.011496d+03,6.061802d+03,6.112528d+03,6.163678d+03,

&6.215257d+03,6.267267d+03,6.319712d+03,6.372597d+03,6.425924d+03,

&6.479697d+03,6.533920d+03,6.588597d+03,6.643731d+03,6.699327d+03,

&6.755388d+03,6.811918d+03,6.868921d+03,6.926401d+03,6.984362d+03,

&7.042809d+03,7.101744d+03,7.161172d+03,7.221098d+03,7.281525d+03,

&7.342458d+03,7.403901d+03,7.465858d+03,7.528334d+03,7.591332d+03,

&7.654857d+03,7.718914d+03,7.783507d+03,7.848641d+03,7.914319d+03,

&7.980548d+03,8.047330d+03,8.114671d+03,8.182576d+03,8.251049d+03,

&8.320095d+03,8.389719d+03,8.459926d+03,8.530719d+03,8.602106d+03,

&8.674090d+03,8.746676d+03,8.819869d+03,8.893675d+03,8.968099d+03,

&9.043145d+03,9.118820d+03,9.195127d+03,9.272074d+03,9.349664d+03/

data eg20l/

&9.427903d+03,9.506797d+03,9.586352d+03,9.666572d+03,9.747463d+03,

&9.829031d+03,9.911282d+03,9.994221d+03,1.007785d+04,1.016219d+04,

&1.024723d+04,1.033298d+04,1.041944d+04,1.050664d+04,1.059456d+04,

&1.068321d+04,1.077261d+04,1.086276d+04,1.095366d+04,1.104532d+04,

&1.113775d+04,1.123095d+04,1.132494d+04,1.141970d+04,1.151527d+04,

&1.161163d+04,1.170880d+04,1.180678d+04,1.190558d+04,1.200521d+04,

&1.210567d+04,1.220697d+04,1.230912d+04,1.241212d+04,1.251599d+04,

&1.262073d+04,1.272634d+04,1.283283d+04,1.294022d+04,1.304851d+04,

&1.315770d+04,1.326780d+04,1.337883d+04,1.349079d+04,1.360368d+04,

&1.371752d+04,1.383231d+04,1.394806d+04,1.406478d+04,1.418247d+04,

&1.430116d+04,1.442083d+04,1.454151d+04,1.466319d+04,1.478590d+04,

&1.490963d+04,1.503439d+04,1.516020d+04,1.528706d+04,1.541499d+04,

&1.554398d+04,1.567406d+04,1.580522d+04,1.593748d+04,1.607085d+04,

&1.620533d+04,1.634094d+04,1.647768d+04,1.661557d+04,1.675461d+04,

&1.689482d+04,1.703620d+04,1.717876d+04,1.732251d+04,1.746747d+04,

&1.761364d+04,1.776104d+04,1.790966d+04,1.805953d+04,1.821066d+04,

&1.836305d+04,1.851671d+04,1.867166d+04,1.882791d+04,1.898547d+04,

&1.914434d+04,1.930454d+04,1.946608d+04,1.962898d+04,1.979324d+04,

&1.995887d+04,2.012589d+04,2.029431d+04,2.046413d+04,2.063538d+04/

data eg20m/

&2.080806d+04,2.098218d+04,2.115777d+04,2.133482d+04,2.151335d+04,

&2.169338d+04,2.187491d+04,2.205796d+04,2.224255d+04,2.242868d+04,

&2.261636d+04,2.280562d+04,2.299646d+04,2.318890d+04,2.338295d+04,

&2.357862d+04,2.377593d+04,2.397489d+04,2.417552d+04,2.437782d+04,

&2.458182d+04,2.478752d+04,2.499495d+04,2.520411d+04,2.541502d+04,

&2.562770d+04,2.584215d+04,2.605841d+04,2.627647d+04,2.649635d+04,

&2.671808d+04,2.694166d+04,2.700000d+04,2.716711d+04,2.739445d+04,

&2.762369d+04,2.785485d+04,2.808794d+04,2.832299d+04,2.850000d+04,

&2.856000d+04,2.879899d+04,2.903999d+04,2.928300d+04,2.952804d+04,

&2.977514d+04,3.002430d+04,3.027555d+04,3.052890d+04,3.078437d+04,

&3.104198d+04,3.130174d+04,3.156368d+04,3.182781d+04,3.209415d+04,

&3.236272d+04,3.263353d+04,3.290662d+04,3.318198d+04,3.345965d+04,

&3.373965d+04,3.402199d+04,3.430669d+04,3.459377d+04,3.488326d+04,

&3.517517d+04,3.546952d+04,3.576633d+04,3.606563d+04,3.636743d+04,

&3.667176d+04,3.697864d+04,3.728808d+04,3.760011d+04,3.791476d+04,

&3.823203d+04,3.855196d+04,3.887457d+04,3.919988d+04,3.952791d+04,

&3.985869d+04,4.019223d+04,4.052857d+04,4.086771d+04,4.120970d+04,

&4.155455d+04,4.190229d+04,4.225293d+04,4.260651d+04,4.296305d+04,

&4.332257d+04,4.368510d+04,4.405066d+04,4.441928d+04,4.479099d+04/

data eg20n/

&4.516581d+04,4.554376d+04,4.592488d+04,4.630919d+04,4.669671d+04,

&4.708747d+04,4.748151d+04,4.787884d+04,4.827950d+04,4.868351d+04,

&4.909090d+04,4.950170d+04,4.991594d+04,5.033364d+04,5.075484d+04,

&5.117957d+04,5.160785d+04,5.203971d+04,5.247518d+04,5.291430d+04,

&5.335710d+04,5.380360d+04,5.425384d+04,5.470784d+04,5.516564d+04,

&5.562728d+04,5.609278d+04,5.656217d+04,5.703549d+04,5.751277d+04,

&5.799405d+04,5.847935d+04,5.896871d+04,5.946217d+04,5.995976d+04,

&6.046151d+04,6.096747d+04,6.147765d+04,6.199211d+04,6.251086d+04,

&6.303396d+04,6.356144d+04,6.409333d+04,6.462968d+04,6.517051d+04,

&6.571586d+04,6.626579d+04,6.682031d+04,6.737947d+04,6.794331d+04,

&6.851187d+04,6.908519d+04,6.966330d+04,7.024626d+04,7.083409d+04,

&7.142684d+04,7.202455d+04,7.262726d+04,7.323502d+04,7.384786d+04,

&7.446583d+04,7.508897d+04,7.571733d+04,7.635094d+04,7.698986d+04,

&7.763412d+04,7.828378d+04,7.893887d+04,7.950000d+04,7.959944d+04,

&8.026554d+04,8.093721d+04,8.161451d+04,8.229747d+04,8.250000d+04,

&8.298615d+04,8.368059d+04,8.438084d+04,8.508695d+04,8.579897d+04,

&8.651695d+04,8.724094d+04,8.797098d+04,8.870714d+04,8.944945d+04,

&9.019798d+04,9.095277d+04,9.171388d+04,9.248135d+04,9.325525d+04,

&9.403563d+04,9.482253d+04,9.561602d+04,9.641615d+04,9.722297d+04/

data eg20o/

&9.803655d+04,9.885694d+04,9.968419d+04,1.005184d+05,1.013595d+05,

&1.022077d+05,1.030630d+05,1.039254d+05,1.047951d+05,1.056720d+05,

&1.065563d+05,1.074480d+05,1.083471d+05,1.092538d+05,1.101681d+05,

&1.110900d+05,1.120196d+05,1.129570d+05,1.139022d+05,1.148554d+05,

&1.158165d+05,1.167857d+05,1.177629d+05,1.187484d+05,1.197421d+05,

&1.207441d+05,1.217545d+05,1.227734d+05,1.238008d+05,1.248368d+05,

&1.258814d+05,1.269348d+05,1.279970d+05,1.290681d+05,1.301482d+05,

&1.312373d+05,1.323355d+05,1.334429d+05,1.345596d+05,1.356856d+05,

&1.368210d+05,1.379660d+05,1.391205d+05,1.402847d+05,1.414586d+05,

&1.426423d+05,1.438360d+05,1.450396d+05,1.462533d+05,1.474772d+05,

&1.487113d+05,1.499558d+05,1.512106d+05,1.524760d+05,1.537519d+05,

&1.550385d+05,1.563359d+05,1.576442d+05,1.589634d+05,1.602936d+05,

&1.616349d+05,1.629875d+05,1.643514d+05,1.657268d+05,1.671136d+05,

&1.685120d+05,1.699221d+05,1.713441d+05,1.727779d+05,1.742237d+05,

&1.756817d+05,1.771518d+05,1.786342d+05,1.801291d+05,1.816364d+05,

&1.831564d+05,1.846891d+05,1.862346d+05,1.877930d+05,1.893645d+05,

&1.909491d+05,1.925470d+05,1.941583d+05,1.957830d+05,1.974214d+05,

&1.990734d+05,2.007393d+05,2.024191d+05,2.041130d+05,2.058210d+05,

&2.075434d+05,2.092801d+05,2.110314d+05,2.127974d+05,2.145781d+05/

data eg20p/

&2.163737d+05,2.181844d+05,2.200102d+05,2.218512d+05,2.237077d+05,

&2.255797d+05,2.274674d+05,2.293709d+05,2.312903d+05,2.332258d+05,

&2.351775d+05,2.371455d+05,2.391299d+05,2.411310d+05,2.431488d+05,

&2.451835d+05,2.472353d+05,2.493042d+05,2.513904d+05,2.534941d+05,

&2.556153d+05,2.577544d+05,2.599113d+05,2.620863d+05,2.642794d+05,

&2.664910d+05,2.687210d+05,2.709697d+05,2.732372d+05,2.755237d+05,

&2.778293d+05,2.801543d+05,2.824986d+05,2.848626d+05,2.872464d+05,

&2.896501d+05,2.920740d+05,2.945181d+05,2.969826d+05,2.972000d+05,

&2.985000d+05,2.994678d+05,3.019738d+05,3.045008d+05,3.070489d+05,

&3.096183d+05,3.122093d+05,3.148219d+05,3.174564d+05,3.201129d+05,

&3.227916d+05,3.254928d+05,3.282166d+05,3.309631d+05,3.337327d+05,

&3.365254d+05,3.393415d+05,3.421812d+05,3.450446d+05,3.479320d+05,

&3.508435d+05,3.537795d+05,3.567399d+05,3.597252d+05,3.627354d+05,

&3.657708d+05,3.688317d+05,3.719181d+05,3.750304d+05,3.781687d+05,

&3.813333d+05,3.845243d+05,3.877421d+05,3.909868d+05,3.942586d+05,

&3.975578d+05,4.008846d+05,4.042393d+05,4.076220d+05,4.110331d+05,

&4.144727d+05,4.179410d+05,4.214384d+05,4.249651d+05,4.285213d+05,

&4.321072d+05,4.357231d+05,4.393693d+05,4.430460d+05,4.467535d+05,

&4.504920d+05,4.542618d+05,4.580631d+05,4.618963d+05,4.657615d+05/

data eg20q/

&4.696591d+05,4.735892d+05,4.775523d+05,4.815485d+05,4.855782d+05,

&4.896416d+05,4.937390d+05,4.978707d+05,5.020369d+05,5.062381d+05,

&5.104743d+05,5.147461d+05,5.190535d+05,5.233971d+05,5.277769d+05,

&5.321934d+05,5.366469d+05,5.411377d+05,5.456660d+05,5.502322d+05,

&5.548366d+05,5.594796d+05,5.641614d+05,5.688824d+05,5.736429d+05,

&5.784432d+05,5.832837d+05,5.881647d+05,5.930866d+05,5.980496d+05,

&6.030542d+05,6.081006d+05,6.131893d+05,6.183206d+05,6.234948d+05,

&6.287123d+05,6.339734d+05,6.392786d+05,6.446282d+05,6.500225d+05,

&6.554620d+05,6.609470d+05,6.664779d+05,6.720551d+05,6.776790d+05,

&6.833499d+05,6.890683d+05,6.948345d+05,7.006490d+05,7.065121d+05,

&7.124243d+05,7.183860d+05,7.243976d+05,7.304594d+05,7.365720d+05,

&7.427358d+05,7.489511d+05,7.552184d+05,7.615382d+05,7.679109d+05,

&7.743369d+05,7.808167d+05,7.873507d+05,7.939393d+05,8.005831d+05,

&8.072825d+05,8.140380d+05,8.208500d+05,8.277190d+05,8.346455d+05,

&8.416299d+05,8.486728d+05,8.557746d+05,8.629359d+05,8.701570d+05,

&8.774387d+05,8.847812d+05,8.921852d+05,8.996511d+05,9.071795d+05,

&9.147709d+05,9.224259d+05,9.301449d+05,9.379285d+05,9.457772d+05,

&9.536916d+05,9.616723d+05,9.697197d+05,9.778344d+05,9.860171d+05,

&9.942682d+05,1.002588d+06,1.010978d+06,1.019438d+06,1.027969d+06/

data eg20r/

&1.036571d+06,1.045245d+06,1.053992d+06,1.062812d+06,1.071706d+06,

&1.080674d+06,1.089717d+06,1.098836d+06,1.108032d+06,1.117304d+06,

&1.126654d+06,1.136082d+06,1.145588d+06,1.155175d+06,1.164842d+06,

&1.174589d+06,1.184418d+06,1.194330d+06,1.204324d+06,1.214402d+06,

&1.224564d+06,1.234812d+06,1.245145d+06,1.255564d+06,1.266071d+06,

&1.276666d+06,1.287349d+06,1.298122d+06,1.308985d+06,1.319938d+06,

&1.330984d+06,1.342122d+06,1.353353d+06,1.364678d+06,1.376098d+06,

&1.387613d+06,1.399225d+06,1.410934d+06,1.422741d+06,1.434646d+06,

&1.446652d+06,1.458758d+06,1.470965d+06,1.483274d+06,1.495686d+06,

&1.508202d+06,1.520823d+06,1.533550d+06,1.546383d+06,1.559323d+06,

&1.572372d+06,1.585530d+06,1.598797d+06,1.612176d+06,1.625667d+06,

&1.639271d+06,1.652989d+06,1.666821d+06,1.680770d+06,1.694834d+06,

&1.709017d+06,1.723318d+06,1.737739d+06,1.752281d+06,1.766944d+06,

&1.781731d+06,1.796640d+06,1.811675d+06,1.826835d+06,1.842122d+06,

&1.857538d+06,1.873082d+06,1.888756d+06,1.904561d+06,1.920499d+06,

&1.936570d+06,1.952776d+06,1.969117d+06,1.985595d+06,2.002210d+06,

&2.018965d+06,2.035860d+06,2.052897d+06,2.070076d+06,2.087398d+06,

&2.104866d+06,2.122480d+06,2.140241d+06,2.158151d+06,2.176211d+06,

&2.194421d+06,2.212785d+06,2.231302d+06,2.249973d+06,2.268802d+06/

data eg20s/

&2.287787d+06,2.306932d+06,2.326237d+06,2.345703d+06,2.365332d+06,

&2.385126d+06,2.405085d+06,2.425211d+06,2.445505d+06,2.465970d+06,

&2.486605d+06,2.507414d+06,2.528396d+06,2.549554d+06,2.570889d+06,

&2.592403d+06,2.614096d+06,2.635971d+06,2.658030d+06,2.680272d+06,

&2.702701d+06,2.725318d+06,2.748124d+06,2.771121d+06,2.794310d+06,

&2.817693d+06,2.841272d+06,2.865048d+06,2.889023d+06,2.913199d+06,

&2.937577d+06,2.962159d+06,2.986947d+06,3.011942d+06,3.037147d+06,

&3.062562d+06,3.088190d+06,3.114032d+06,3.140091d+06,3.166368d+06,

&3.192864d+06,3.219583d+06,3.246525d+06,3.273692d+06,3.301087d+06,

&3.328711d+06,3.356566d+06,3.384654d+06,3.412978d+06,3.441538d+06,

&3.470337d+06,3.499377d+06,3.528661d+06,3.558189d+06,3.587965d+06,

&3.617989d+06,3.648265d+06,3.678794d+06,3.709579d+06,3.740621d+06,

&3.771924d+06,3.803488d+06,3.835316d+06,3.867410d+06,3.899773d+06,

&3.932407d+06,3.965314d+06,3.998497d+06,4.031957d+06,4.065697d+06,

&4.099719d+06,4.134026d+06,4.168620d+06,4.203504d+06,4.238679d+06,

&4.274149d+06,4.309916d+06,4.345982d+06,4.382350d+06,4.419022d+06,

&4.456001d+06,4.493290d+06,4.530890d+06,4.568805d+06,4.607038d+06,

&4.645590d+06,4.684465d+06,4.723666d+06,4.763194d+06,4.803053d+06,

&4.843246d+06,4.883775d+06,4.924643d+06,4.965853d+06,5.007408d+06/

data eg20t/

&5.049311d+06,5.091564d+06,5.134171d+06,5.177135d+06,5.220458d+06,

&5.264143d+06,5.308195d+06,5.352614d+06,5.397406d+06,5.442572d+06,

&5.488116d+06,5.534042d+06,5.580351d+06,5.627049d+06,5.674137d+06,

&5.721619d+06,5.769498d+06,5.817778d+06,5.866462d+06,5.915554d+06,

&5.965056d+06,6.014972d+06,6.065307d+06,6.116062d+06,6.167242d+06,

&6.218851d+06,6.270891d+06,6.323367d+06,6.376282d+06,6.429639d+06,

&6.483443d+06,6.537698d+06,6.592406d+06,6.647573d+06,6.703200d+06,

&6.759294d+06,6.815857d+06,6.872893d+06,6.930406d+06,6.988401d+06,

&7.046881d+06,7.105850d+06,7.165313d+06,7.225274d+06,7.285736d+06,

&7.346704d+06,7.408182d+06,7.470175d+06,7.532687d+06,7.595721d+06,

&7.659283d+06,7.723377d+06,7.788008d+06,7.853179d+06,7.918896d+06,

&7.985162d+06,8.051983d+06,8.119363d+06,8.187308d+06,8.255820d+06,

&8.324906d+06,8.394570d+06,8.464817d+06,8.535652d+06,8.607080d+06,

&8.679105d+06,8.751733d+06,8.824969d+06,8.898818d+06,8.973284d+06,

&9.048374d+06,9.124092d+06,9.200444d+06,9.277435d+06,9.355070d+06,

&9.433354d+06,9.512294d+06,9.591895d+06,9.672161d+06,9.753099d+06,

&9.834715d+06,9.917013d+06,1.000000d+07,1.008368d+07,1.016806d+07,

&1.025315d+07,1.033895d+07,1.042547d+07,1.051271d+07,1.060068d+07,

&1.068939d+07,1.077884d+07,1.086904d+07,1.095999d+07,1.105171d+07/

data eg20u/

&1.114419d+07,1.123745d+07,1.133148d+07,1.142631d+07,1.152193d+07,

&1.161834d+07,1.171557d+07,1.181360d+07,1.191246d+07,1.201215d+07,

&1.211267d+07,1.221403d+07,1.231624d+07,1.241930d+07,1.252323d+07,

&1.262802d+07,1.273370d+07,1.284025d+07,1.294770d+07,1.305605d+07,

&1.316531d+07,1.327548d+07,1.338657d+07,1.349859d+07,1.361155d+07,

&1.372545d+07,1.384031d+07,1.395612d+07,1.407291d+07,1.419068d+07,

&1.430943d+07,1.442917d+07,1.454991d+07,1.467167d+07,1.479444d+07,

&1.491825d+07,1.504309d+07,1.516897d+07,1.529590d+07,1.542390d+07,

&1.555297d+07,1.568312d+07,1.581436d+07,1.594670d+07,1.608014d+07,

&1.621470d+07,1.635039d+07,1.648721d+07,1.662518d+07,1.676430d+07,

&1.690459d+07,1.704605d+07,1.718869d+07,1.733253d+07,1.747757d+07,

&1.762383d+07,1.777131d+07,1.792002d+07,1.806998d+07,1.822119d+07,

&1.837367d+07,1.852742d+07,1.868246d+07,1.883880d+07,1.899644d+07,

&1.915541d+07,1.931570d+07,1.947734d+07,1.964033d+07/

data eg21a/

&1.000010d-05,1.100000d-04,3.000000d-03,5.500100d-03,1.000000d-02,

&1.500000d-02,2.000000d-02,3.000000d-02,3.200000d-02,3.238000d-02,

&4.300000d-02,5.900100d-02,7.700100d-02,9.500000d-02,1.000000d-01,

&1.150000d-01,1.340000d-01,1.600000d-01,1.890000d-01,2.200000d-01,

&2.480000d-01,2.825000d-01,3.145000d-01,3.520000d-01,3.910100d-01,

&4.139900d-01,4.330000d-01,4.850100d-01,5.315800d-01,5.400100d-01,

&6.250100d-01,6.825600d-01,7.050000d-01,7.900100d-01,8.600100d-01,

&8.764200d-01,9.300100d-01,9.860100d-01,1.010000d+00,1.035000d+00,

&1.070000d+00,1.080000d+00,1.090000d+00,1.110000d+00,1.125400d+00,

&1.170000d+00,1.235000d+00,1.305000d+00,1.370000d+00,1.440000d+00,

&1.445000d+00,1.510000d+00,1.590000d+00,1.670000d+00,1.755000d+00,

&1.840000d+00,1.855400d+00,1.930000d+00,2.020000d+00,2.130000d+00,

&2.360000d+00,2.372400d+00,2.767900d+00,3.059000d+00,3.380700d+00,

&3.927900d+00,4.129200d+00,4.470000d+00,4.670000d+00,5.043500d+00,

&5.623000d+00,6.160100d+00,6.476000d+00,7.079000d+00,7.524000d+00,

&7.943000d+00,8.315300d+00,8.913000d+00,9.189800d+00,1.000000d+01,

&1.067700d+01,1.122400d+01,1.259000d+01,1.371000d+01,1.522700d+01,

&1.674500d+01,1.760300d+01,1.902800d+01,2.045200d+01,2.260300d+01,

&2.498000d+01,2.791800d+01,2.920300d+01,3.051100d+01,3.388900d+01/

data eg21b/

&3.726700d+01,3.981000d+01,4.551700d+01,4.785100d+01,5.012000d+01,

&5.559500d+01,6.144200d+01,6.310000d+01,6.790400d+01,7.079000d+01,

&7.889300d+01,8.527700d+01,9.166100d+01,1.013000d+02,1.122000d+02,

&1.300700d+02,1.367400d+02,1.585000d+02,1.670200d+02,1.778000d+02,

&2.039900d+02,2.144500d+02,2.430100d+02,2.753600d+02,3.043200d+02,

&3.535800d+02,3.981000d+02,4.540000d+02,5.144600d+02,5.829500d+02,

&6.310000d+02,6.772900d+02,7.079000d+02,7.485200d+02,8.482000d+02,

&9.611200d+02,1.010400d+03,1.116700d+03,1.234100d+03,1.363900d+03,

&1.507300d+03,1.584600d+03,1.795600d+03,2.034700d+03,2.113000d+03,

&2.248700d+03,2.371000d+03,2.485200d+03,2.612600d+03,2.661000d+03,

&2.746500d+03,2.818000d+03,3.035400d+03,3.162000d+03,3.354600d+03,

&3.548000d+03,3.707400d+03,3.981000d+03,4.307400d+03,4.642900d+03,

&5.004500d+03,5.530800d+03,6.267300d+03,7.101700d+03,7.465900d+03,

&8.251000d+03,9.118800d+03,1.007800d+04,1.113800d+04,1.170900d+04,

&1.272600d+04,1.383200d+04,1.503400d+04,1.585000d+04,1.661600d+04,

&1.778000d+04,1.930500d+04,1.995000d+04,2.054000d+04,2.113000d+04,

&2.187500d+04,2.239000d+04,2.304000d+04,2.357900d+04,2.417600d+04,

&2.441000d+04,2.478800d+04,2.512000d+04,2.585000d+04,2.605800d+04,

&2.661000d+04,2.700000d+04,2.738000d+04,2.818000d+04,2.850000d+04/

data eg21c/

&2.901000d+04,2.985000d+04,3.073000d+04,3.162000d+04,3.182800d+04,

&3.430700d+04,3.697900d+04,4.086800d+04,4.358900d+04,4.630900d+04,

&4.939200d+04,5.247500d+04,5.516600d+04,5.656200d+04,6.172500d+04,

&6.737900d+04,7.200000d+04,7.499000d+04,7.950000d+04,8.229700d+04,

&8.250000d+04,8.651700d+04,9.803700d+04,1.110900d+05,1.167900d+05,

&1.227700d+05,1.290700d+05,1.356900d+05,1.426400d+05,1.499600d+05,

&1.576400d+05,1.657300d+05,1.742200d+05,1.831600d+05,1.925500d+05,

&2.024200d+05,2.128000d+05,2.237100d+05,2.351800d+05,2.472400d+05,

&2.732400d+05,2.872500d+05,2.945200d+05,2.972000d+05,2.985000d+05,

&3.019700d+05,3.337300d+05,3.688300d+05,3.877400d+05,4.076200d+05,

&4.504900d+05,5.234000d+05,5.502300d+05,5.784400d+05,6.081000d+05,

&6.392800d+05,6.720600d+05,7.065100d+05,7.427400d+05,7.808200d+05,

&8.208500d+05,8.629400d+05,9.071800d+05,9.616400d+05,1.002600d+06,

&1.108000d+06,1.164800d+06,1.224600d+06,1.287300d+06,1.353400d+06,

&1.422700d+06,1.495700d+06,1.572400d+06,1.653000d+06,1.737700d+06,

&1.826800d+06,1.920500d+06,2.019000d+06,2.122500d+06,2.231300d+06,

&2.306900d+06,2.345700d+06,2.365300d+06,2.385200d+06,2.466000d+06,

&2.592400d+06,2.725300d+06,2.865000d+06,3.011900d+06,3.166400d+06,

&3.328700d+06,3.678800d+06,4.065700d+06,4.493300d+06,4.723700d+06/

data eg21d/

&4.965900d+06,5.220500d+06,5.488100d+06,5.769500d+06,6.065300d+06,

&6.376300d+06,6.592400d+06,6.703200d+06,7.046900d+06,7.408200d+06,

&7.788000d+06,8.187300d+06,8.607100d+06,9.048400d+06,9.512300d+06,

&1.000000d+07,1.051300d+07,1.105200d+07,1.161800d+07,1.221400d+07,

&1.284000d+07,1.349900d+07,1.384000d+07,1.419100d+07,1.455000d+07,

&1.491800d+07,1.568300d+07,1.648700d+07,1.690500d+07,1.733300d+07,

&1.964000d+07/

data eg22a/

&1.000010d-05,3.000000d-03,5.000000d-03,6.900000d-03,1.000000d-02,

&1.500000d-02,2.000000d-02,2.500000d-02,3.000000d-02,3.500000d-02,

&4.200000d-02,5.000000d-02,5.800000d-02,6.700000d-02,7.700000d-02,

&8.000000d-02,9.500000d-02,1.000000d-01,1.150000d-01,1.340000d-01,

&1.400000d-01,1.600000d-01,1.800000d-01,1.890000d-01,2.200000d-01,

&2.480000d-01,2.800000d-01,3.000000d-01,3.145000d-01,3.200000d-01,

&3.500000d-01,3.910000d-01,4.000000d-01,4.330000d-01,4.850000d-01,

&5.000000d-01,5.400000d-01,6.250000d-01,7.050000d-01,7.800000d-01,

&7.900000d-01,8.500000d-01,8.600000d-01,9.100000d-01,9.300000d-01,

&9.500000d-01,9.720000d-01,9.860000d-01,9.960000d-01,1.020000d+00,

&1.035000d+00,1.045000d+00,1.071000d+00,1.097000d+00,1.110000d+00,

&1.123000d+00,1.150000d+00,1.170000d+00,1.235000d+00,1.300000d+00,

&1.337500d+00,1.370000d+00,1.440000d+00,1.475000d+00,1.500000d+00,

&1.590000d+00,1.670000d+00,1.755000d+00,1.840000d+00,1.930000d+00,

&2.020000d+00,2.100000d+00,2.130000d+00,2.360000d+00,2.550000d+00,

&2.600000d+00,2.720000d+00,2.767920d+00,3.300000d+00,3.380750d+00,

&4.000000d+00,4.129250d+00,5.043477d+00,5.346430d+00,6.160116d+00,

&7.523983d+00,8.315287d+00,9.189814d+00,9.905554d+00,1.122446d+01,

&1.370959d+01,1.592827d+01,1.945484d+01,2.260329d+01,2.498050d+01/

data eg22b/

&2.760773d+01,3.051126d+01,3.372015d+01,3.726653d+01,4.016900d+01,

&4.551744d+01,4.825160d+01,5.157802d+01,5.559513d+01,6.790405d+01,

&7.567357d+01,9.166088d+01,1.367420d+02,1.486254d+02,2.039950d+02,

&3.043248d+02,3.717032d+02,4.539993d+02,6.772874d+02,7.485183d+02,

&9.142423d+02,1.010394d+03,1.234098d+03,1.433817d+03,1.507331d+03,

&2.034684d+03,2.248673d+03,3.354626d+03,3.526622d+03,5.004514d+03,

&5.530844d+03,7.465858d+03,9.118820d+03,1.113775d+04,1.503439d+04,

&1.661557d+04,2.478752d+04,2.739445d+04,2.928300d+04,3.697864d+04,

&4.086771d+04,5.516564d+04,6.737947d+04,8.229747d+04,1.110900d+05,

&1.227734d+05,1.831564d+05,2.472353d+05,2.732372d+05,3.019738d+05,

&4.076220d+05,4.504920d+05,4.978707d+05,5.502322d+05,6.081006d+05,

&8.208500d+05,9.071795d+05,1.002588d+06,1.108032d+06,1.224564d+06,

&1.353353d+06,1.652989d+06,2.018965d+06,2.231302d+06,2.465970d+06,

&3.011942d+06,3.678794d+06,4.493290d+06,5.488116d+06,6.065307d+06,

&6.703200d+06,8.187308d+06,1.000000d+07,1.1618343d+07,

&1.3840307d+07,1.4918247d+07,1.733253d+07,1.964033d+07/

data eg23a/

&1.000010d-05,1.000010d-01,4.139940d-01,5.315790d-01,6.825600d-01,

&8.764250d-01,1.123000d+00,1.440000d+00,1.855390d+00,2.382370d+00,

&3.059020d+00,3.927860d+00,5.043480d+00,6.475950d+00,8.315290d+00,

&1.067700d+01,1.370960d+01,1.760350d+01,2.260330d+01,2.902320d+01,

&3.726650d+01,4.785120d+01,6.144210d+01,7.889320d+01,1.013010d+02,

&1.300730d+02,1.670170d+02,2.144540d+02,2.753640d+02,3.535750d+02,

&4.539990d+02,5.829470d+02,7.485180d+02,9.611170d+02,1.234100d+03,

&1.584610d+03,2.034680d+03,2.248670d+03,2.485170d+03,2.612590d+03,

&2.746540d+03,3.035390d+03,3.354630d+03,3.707440d+03,4.307420d+03,

&5.530840d+03,7.101740d+03,9.118820d+03,1.059460d+04,1.170880d+04,

&1.503440d+04,1.930450d+04,2.187490d+04,2.357860d+04,2.417550d+04,

&2.478750d+04,2.605840d+04,2.700010d+04,2.850110d+04,3.182780d+04,

&3.430670d+04,4.086770d+04,4.630920d+04,5.247520d+04,5.656220d+04,

&6.737950d+04,7.202450d+04,7.949870d+04,8.250340d+04,8.651700d+04,

&9.803650d+04,1.110900d+05,1.167860d+05,1.227730d+05,1.290680d+05,

&1.356860d+05,1.426420d+05,1.499560d+05,1.576440d+05,1.657270d+05,

&1.742240d+05,1.831560d+05,1.925470d+05,2.024190d+05,2.127970d+05,

&2.237080d+05,2.351770d+05,2.472350d+05,2.732370d+05,2.872460d+05,

&2.945180d+05,2.972110d+05,2.984910d+05,3.019740d+05,3.337330d+05/

data eg23b/

&3.688320d+05,3.877420d+05,4.076220d+05,4.504920d+05,4.978710d+05,

&5.233970d+05,5.502320d+05,5.784430d+05,6.081010d+05,6.392790d+05,

&6.720550d+05,7.065120d+05,7.427360d+05,7.808170d+05,8.208500d+05,

&8.629360d+05,9.071800d+05,9.616720d+05,1.002590d+06,1.108030d+06,

&1.164840d+06,1.224560d+06,1.287350d+06,1.353350d+06,1.422740d+06,

&1.495690d+06,1.572370d+06,1.652990d+06,1.737740d+06,1.826840d+06,

&1.920500d+06,2.018970d+06,2.122480d+06,2.231300d+06,2.306930d+06,

&2.345700d+06,2.365330d+06,2.385130d+06,2.465970d+06,2.592400d+06,

&2.725320d+06,2.865050d+06,3.011940d+06,3.166370d+06,3.328710d+06,

&3.678790d+06,4.065700d+06,4.493290d+06,4.723670d+06,4.965850d+06,

&5.220460d+06,5.488120d+06,5.769500d+06,6.065310d+06,6.376280d+06,

&6.592410d+06,6.703200d+06,7.046880d+06,7.408180d+06,7.788010d+06,

&8.187310d+06,8.607080d+06,9.048370d+06,9.512290d+06,1.000000d+07,

&1.051270d+07,1.105170d+07,1.161830d+07,1.221400d+07,1.252320d+07,

&1.284030d+07,1.349860d+07,1.384030d+07,1.419070d+07,1.454990d+07,

&1.491820d+07,1.568310d+07,1.648720d+07,1.690460d+07,1.733250d+07,

&1.964030d+07/

*b groupr.1837

c

c     ***ecco  33-group structure

else if (ign.eq.19) then

ng=33

do ig=1,34

eg(ig)=eg19(ig)

enddo

c

c     ***ecco 1968-group structure

else if (ign.eq.20) then

ng=1968

do ig=1,1969

eg(ig)=eg20(ig)

enddo

c

c     ***tripoli 315-group structure

else if (ign.eq.21) then

ng=315

do ig=1,316

eg(ig)=eg21(ig)

enddo

c

c     ***xmas LWPC 172-group structure

else if (ign.eq.22) then

ng=172

do ig=1,173

eg(ig)=eg22(ig)

enddo

c

c     ***vit-J LWPC 175-group structure

else if (ign.eq.23) then

ng=175

do ig=1,176

eg(ig)=eg23(ig)

enddo

*b groupr.1888

if (ign.eq.19) write(nsyso,'(/

&  '' neutron group structure......ecco  33-group'')')

if (ign.eq.20) write(nsyso,'(/

&  '' neutron group structure......ecco  1968-group'')')

if (ign.eq.21) write(nsyso,'(/

&  '' neutron group structure......tripoli 315-group'')')

if (ign.eq.22) write(nsyso,'(/

&  '' neutron group structure......xmas LWPC 172-group'')')

if (ign.eq.23) write(nsyso,'(/

&  '' neutron group structure......vit-J LWPC 175-group'')')

*/

*/ increase the size of egn from 641 to 15000 i.e DICE 13193 APOLLO 11276

*/

*d groupr.1643

data ngmax/15000/

*d groupr.228

common/groupn/ign,ngn,egn(15000)

*d groupr.772

common/groupn/ign,ngn,egn(15000)

*d groupr.1303

common/groupn/ign,ng,eg(15000)

*d groupr.2643

common/groupn/ig,ngn,egn(15000)

*d groupr.3074

common/groupn/ign,ngn,egn(15000)

*d groupr.4274

common/groupn/ign,ngn,egn(15000)

*d groupr.6415

common/groupn/ign,ngn,egn(15000)

*d groupr.6918

common/groupn/ign,ngn,egn(15000)

*/

## C.10 upn_Shimizu

REM upn_Shimizu  : upshim (included in ADS)

*/

*/ Kazuaki Kosako, Shimizu Corporation

*/ MF5 and MF6 INT=21-25 laws modifications

*/ in groupr

*/

*ident upshim

*/

*i groupr.548

ee=0

*d groupr.550

*/

*/*d groupr.5586

*/      dimension cnow(*),p(64)

*i groupr.5668

if (na.gt.64)  call error('f6ddx',

&                   'order of legendre expansion > 64  ','  ')

*/*d groupr.5768

*/      dimension cnow(*),p(64)

*i groupr.5811

if (na.gt.64)  call error('f6dis',

&                   'order of legendre expansion > 64  ','  ')

*i groupr.8641

parameter (npmax=15001,npmax0=npmax-1,mxset=200,mxnrf1=50)

common/mainio/nsysi,nsyso,nsyse,ntty

common/nalf5a/npf1(mxset),nbtf1(mxnrf1),intf1(mxnrf1)

common/nalf5b/eintf1(mxset),xdatwk(npmax),xdatf1(npmax,mxset),

1              ansf1(npmax),ydatwk(npmax),ydatf1(npmax,mxset),

2              epmax(mxset)

*i groupr.8647

external f5xlin,f5xint

*i groupr.8750

nr=nint(c(l+4))

intchk=0

do k=1,nr

intnow=nint(c(nnt+ic-1+2*k))

if (intnow.le.0.or.(intnow.gt.6.and.intnow.le.20).or.

&                intnow.gt.25) then

write(strng,'(a,i6)') 'int=',intnow

call error('getsed','interplation error',strng)

endif

if (intnow.gt.intchk) intchk=intnow

enddo

*i groupr.8767

if (intchk.ge.21.and.intchk.le.25) then

if (nne.gt.mxset)

&               call error('getsed','storage exceeded - nne',' ')

eintf1(nne)=c(iraw+1)

npnow=nint(c(iraw+5))

nrf1=nint(c(iraw+4))

if (npnow.gt.npmax0)

&               call error('getsed','storage exceeded - npnow',' ')

if (nrf1.gt.mxnrf1)

&               call error('getsed','storage exceeded - nrf1',' ')

intone=0

do j=1,nrf1

nbtf1(j)=nint(c(iraw+4+2*j))

intf1(j)=nint(c(iraw+5+2*j))

if (intf1(j).eq.1) intone=1

enddo

do i=1,npmax

xdatwk(i)=0

ydatwk(i)=0

enddo

ipos=iraw+6+2*nrf1

do j=1,npnow

isw1=ipos+2*(j-1)

xdatwk(j)=c(isw1)

ydatwk(j)=c(isw1+1)

enddo

emaxf1=xdatwk(npnow)

epmax(nne)=emaxf1

do j=1,npnow

xdatwk(j)=xdatwk(j)/emaxf1

ydatwk(j)=ydatwk(j)*emaxf1

enddo

if (xdatwk(1).gt.zero.and.intf1(1).eq.1) then

if (ydatwk(1).eq.zero) xdatwk(1)=0

endif

c

npnew=0

call f5xlin(nbtf1,intf1,nrf1,xdatwk,ydatwk,npnow,

&                        xdatf1(1,nne),ydatf1(1,nne),npmax0,npnew,

&                        nsyso)

sumf1=0

npf1(nne)=npnew

if (intone.eq.1) then

do j=2,npf1(nne)-2

if (xdatf1(j,nne).eq.xdatf1(j+1,nne)) then

s1=xdatf1(j,nne)*0.999995d+0

s2=xdatf1(j,nne)*1.000005d+0

if (xdatf1(j-1,nne).lt.s1) xdatf1(j,nne)=s1

if (xdatf1(j+2,nne).gt.s2) xdatf1(j+1,nne)=s2

endif

enddo

endif

do j=2,npf1(nne)

sumf1=sumf1+(xdatf1(j,nne)-xdatf1(j-1,nne))*

&                     (ydatf1(j,nne)+ydatf1(j-1,nne))/2

enddo

xdatf1(npnew+1,nne)=0

ydatf1(npnew+1,nne)=0

anorm=1

if (sumf1.gt.zero) anorm=1/sumf1

do j=1,npf1(nne)

ydatf1(j,nne)=anorm*ydatf1(j,nne)

enddo

endif

*i groupr.8782

if (intchk.ge.21.and.intchk.le.25) then

econst=0

else

*i groupr.8813

endif

*i groupr.8903

if (int.ge.21.and.int.le.25) then

call f5xint(ed,sed,eg,ng,nk,matd,mfd,ne,int,nne,

&                           ikt,elo,ehi,pe,nsyso)

else

*i groupr.8907

endif

*i groupr.8966

subroutine f5xlin(nbt,int,n1,xin,yin,n2,xout,yout,npmax,npout,

1                  nsyso)

c     ******************************************************************

c     convert data to linear-linear form.

c     originality of this routine is subroutine filex in the linear-2000

c     code.

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

external error,terp1,sigfig

save xcmin,errx,half

dimension xin(n2),yin(n2),xout(npmax),yout(npmax)

dimension nbt(n1),int(n1)

*if sw

data xcmin/1.0d-15/

data errx/5.0d-4/

data half/0.5d0/

*else

data xcmin/1.0e-15/

data errx/5.0e-4/

data half/0.5e0/

*endif

c

c-----initialize count of points in core and on scratch.

n2core=1

zero=0

c-----define first point in table.

xout(1)=xin(1)

yout(1)=yin(1)

c-----set flag to indicate if this is a threshold reaction.

ithres=0

if (yout(1).le.xcmin) ithres=1

n2p1=2

n2p2=3

c-----set up loop over interpolation ranges.

nr2=1

do 400 ir=1,n1

c-----define points in interpolation range and type of interpolation.

nr1=nr2+1

nr2=nbt(ir)

intype=int(ir)

c-----data check

minus=0

do i=nr1,nr2

if (yin(i).le.zero) minus=1

enddo

c

if (intype.gt.3.and.minus.eq.1) intype=2

c

c     non-linear interpolation law requires sub-division. set up loop

c     over points in current interpolation region.

c

c     interpolation law branch.

if (intype-2) 50,80,100

c

c     for histogram replace each energy point that is internal to the

c     interpolation energy range by two energy points and replace each

c     end point of the interpolation energy range by a single energy

c     point (start of interval has already been stored).

c

50 continue

do 70 npt=nr1,nr2

n2core=n2core+2

if (n2core.gt.npmax) call error('f5xlin','storage exceeded',' ')

xout(n2core)=xin(npt)

yout(n2core)=yin(npt)

c-----eliminate duplicate points.

if (xout(n2core).ne.xout(n2core-2)) go to 60

xout(n2core-1)=xout(n2core)

yout(n2core-1)=yout(n2core)

n2core=n2core-1

n2p1=n2core+1

n2p2=n2p1+1

go to 70

60 continue

xout(n2core-1)=xout(n2core)

yout(n2core-1)=yout(n2core-2)

70 continue

n2core=n2core-1

if (ir.lt.n1) then

n2core=n2core+1

if (n2core.gt.npmax)

&      call error('f5xlin','storage exceeded - n2core',' ')

xout(n2core)=xin(nr2)

yout(n2core)=yin(nr2)

endif

n2p1=n2core+1

n2p2=n2p1+1

go to 400

c

c     for linear-linear interpolation just copy points to output array.

c

80 continue

do 90 npt=nr1,nr2

c-----core space for one more point required. if no room in core, thin

n2core=n2core+1

if (n2core.gt.npmax)

&   call error('f5xlin','storage exceeded - n2core',' ')

xout(n2core)=xin(npt)

yout(n2core)=yin(npt)

90 continue

n2p1=n2core+1

n2p2=n2p1+1

go to 400

c

c     non-linear interpolation law requires sub-division. set up loop

c     over points in current interpolation region.

c

100 continue

do 300 npt=nr1,nr2

c-----initialize to range not saved

imsaved=0

c-----define upper energy limit of interval.

xend=xin(npt)

yend=yin(npt)

c     if necessary insert max. energy or thermal point

130 continue

xtop=xend

if (xout(n2core).le.zero) go to 150

if (xtop.gt.2*xout(n2core)) xtop=2*xout(n2core)

if (xtop.ge.xend) go to 150

c-----interpolate cross section to new end

call terp1(xout(n2core),yout(n2core),xend,yend,xtop,ytop,intype)

c-----save end and set range saved flag

imsaved=1

xsave=xend

ysave=yend

c-----define end of interval at thermal

xend=xtop

yend=ytop

c-----define energy and cross section at two ends of interval.

150 continue

xn2p2=xend

yn2p2=yend

xn2=xout(n2core)

yn2=yout(n2core)

c-----do not subdivide if cross section is constant.

if (yn2.eq.yn2p2) go to 220

c

c     do not sub-divide intervals within which the absolute value of

c     the cross section is less than the minimum cross section of

c     interest, accept near thresholds.

c

c-----if this is a threshold reaction do not use low cross section

c-----cutoff criteria in the vacinity of the threshold.

if (ithres.eq.0) go to 160

if (abs(yn2).lt.xcmin) go to 170

ithres=0

go to 170

c-----assume convergence if the absolute value of the cross section

c-----at both ends of the interval is less than the minimum cross

c-----section of interest.

160 continue

if (abs(yn2).le.xcmin.and.abs(yn2p2).le.xcmin) go to 220

c

c     define energy at middle of interval.

c

c-----intype is now 3, 4, 5 or 6.

170 continue

if (intype-4) 190,180,190

c-----linear energy.

180 continue

xn2p1=half*(xn2+xn2p2)

go to 200

190 continue

xn2p1=sqrt(xn2*xn2p2)

c-----round midpoint.

200 continue

xn2p1=sigfig(xn2p1,7,0)

c

c     small energy interval convergence tests.

c

c-----if energy at middle of interval is less than allowable energy

c-----spacing only keep the two ends of the interval.

if (xn2p1.le.xn2.or.xn2p1.ge.xn2p2) go to 220

c

c     define cross section at middle of interval by interpolation law

c     and linear-linear interpolation.

c

call terp1(xn2,yn2,xn2p2,yn2p2,xn2p1,yn2p1,intype)

call terp1(xn2,yn2,xn2p2,yn2p2,xn2p1,yaprox,2)

c

c-----test for convergence. if convergence keep midpoint of interval

c-----in order to allow accurate backward thinning before output.

if (abs(yn2p1-yaprox).le.abs(yn2p1*errx)) go to 210

c

c     no convergence. shorten interval.

c

xn2p2=xn2p1

yn2p2=yn2p1

go to 170

c

c     convergence. keep interval midpoint if backward thinning will be

c     performed. otherwise only keep ends of interval.

c

210 continue

if (n2p2.gt.npmax)

&   call error('f5xlin','storage exceeded - n2p2',' ')

c-----keep interval midpoint and endpoint.

xout(n2p1)=xn2p1

yout(n2p1)=yn2p1

xout(n2p2)=xn2p2

yout(n2p2)=yn2p2

n2core=n2p2

n2p1=n2core+1

n2p2=n2p1+1

go to 230

c-----core space for one more point required. if no room in core, thin

c-----and unload one page of points to scratch.

220 continue

if(n2p1.gt.npmax)

&  call error('f5xlin','storage exceeded - n2p1',' ')

c-----midpoint of interval is not required. only keep endpoint of

c-----interval.

xout(n2p1)=xn2p2

yout(n2p1)=yn2p2

n2core=n2p1

n2p1=n2core+1

n2p2=n2p1+1

c-----if not end of current interval continue. otherwise

c-----move to next interval.

230 continue

if (xout(n2core).lt.xend) go to 150

c-----if range saved, restore point and reset flag

if (imsaved.le.0) go to 300

imsaved=0

xend=xsave

yend=ysave

go to 130

300 continue

c

400 continue

npout=n2core

return

end

c

subroutine f5xint(ed,sed,eg,ng,nk,matd,mfd,ne,int,nne,ikt,elo,ehi,

&                  pe,nsyso )

c     ******************************************************************

c     compute secondary energy distribution for all sink groups

c     simultaneously.  laws 1 with int=21-25 is coded.

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

parameter (npmax=15001,npmax0=npmax-1,mxset=200,mxnrf1=50)

parameter (mxwork=10+2*npmax)

common/nalf5a/npf1(mxset),nbtf1(mxnrf1),intf1(mxnrf1)

common/nalf5b/eintf1(mxset),xdatwk(npmax),xdatf1(npmax,mxset),

1              ansf1(npmax),ydatwk(npmax),ydatf1(npmax,mxset),

2              epmax(mxset)

dimension sed(nk,*),eg(*),c(mxwork)

character strng*60

external error,terp1,intega

save ist,jst1,jst2

*if sw

data small/1.d-10/

data ebig/1.d8/

data zero/0.d0/

*else

data small/1.e-10/

data ebig/1.e8/

data zero/0.e0/

*endif

c

if (nne.ge.ne) nne=ne-1

nne1=nne+1

npnow=npf1(nne)

ist=2

if (xdatf1(1,nne).ne.zero) then

write(strng,'(a,i6)') 'xdatf1(1,nne).ne.0  nne=',nne

call error('f5xint','invalid evaluation data',strng)

elseif (xdatf1(1,nne1).ne.zero) then

write(strng,'(a,i6)') 'xdatf1(1,nne1).ne.0  nne1=',nne1

call error('f5xint','invalid evaluation data',strng)

endif

c

c     make union relative secondary nuetron energy mesh

c     at requested energy range ( eintf1(nne) & eintf1(nne1) )

c

do i=1,npmax

xdatwk(i)=0

ydatwk(i)=0

enddo

do i=1,npnow

xdatwk(i)=xdatf1(i,nne)

enddo

c

do 170 j=2,npf1(nne1)-1

enow=xdatf1(j,nne1)

iadd=0

do i=ist,npnow

ehinow=xdatwk(i)

elonow=xdatwk(i-1)

ratio=1

if (ehinow.gt.zero) ratio=enow/ehinow-1

if (abs(ratio).lt.1.000d-5) go to 150

if (enow.gt.elonow.and.enow.lt.ehinow) then

iadd=i

go to 150

endif

enddo

150 continue

if (iadd.ge.ist) then

ratio=xdatwk(iadd)/enow

if (npnow+1.gt.npmax)

&      call error('f5xint','storage exceeded - npnow+1',' ')

do k=iadd,npnow

i=npnow-k+iadd

xdatwk(i+1)=xdatwk(i)

enddo

xdatwk(iadd)=enow

npnow=npnow+1

ist=iadd

endif

170 continue

c

c     interpolate secondary neutron energy distribution at ed energy

c

itype=int-20

np1=npf1(nne)-1

np2=npf1(nne1)-1

jst1=1

jst2=1

eint1=eintf1(nne)

eint2=eintf1(nne1)

c

c  *** set maximum energy of secondary neutron

c

epmax1=epmax(nne)

epmax2=epmax(nne1)

epmaxn=0

call terp1(eint1,epmax1,eint2,epmax2,ed,epmaxn,2)

sumf1=0

eold=0

yold=0

c

do 200 i=1,npnow

enow=xdatwk(i)

ynow1=0

ynow2=0

do j=jst1,np1

jpos=j

if (enow.ge.xdatf1(j,nne).and.enow.lt.xdatf1(j+1,nne))

&      go to 180

enddo

jpos=np1

180 continue

jpos1=jpos+1

jst1=jpos

x1=xdatf1(jpos,nne)

y1=ydatf1(jpos,nne)

x2=xdatf1(jpos1,nne)

y2=ydatf1(jpos1,nne)

call terp1(x1,y1,x2,y2,enow,ynow1,2)

do j=jst2,np2

jpos=j

if (enow.ge.xdatf1(j,nne1).and.enow.lt.xdatf1(j+1,nne1))

&      go to 190

enddo

jpos=np2

190 continue

jpos1=jpos+1

jst2=jpos

x1=xdatf1(jpos,nne1)

y1=ydatf1(jpos,nne1)

x2=xdatf1(jpos1,nne1)

y2=ydatf1(jpos1,nne1)

call terp1(x1,y1,x2,y2,enow,ynow2,2)

ynow=0

call terp1(eint1,ynow1,eint2,ynow2,ed,ynow,itype)

ydatwk(i)=ynow

if (i.gt.1) sumf1=sumf1+(ynow+yold)*(enow-eold)/2

eold=enow

yold=ynow

200 continue

c

c     define final secondary nuetron energy distribution data

c

anorm=1

if (sumf1.gt.zero) anorm=1/sumf1

do i=1,npnow

xdatwk(i)=xdatwk(i)*epmaxn

ydatwk(i)=anorm*ydatwk(i)/epmaxn

enddo

c

c     calculates groupwise secondary nuetron energy distribution data

c

do ig=1,ng

ansf1(ig)=0

enddo

if (xdatwk(npnow).le.eg(2)) then

ansf1(1)=1

factn=1

go to 320

endif

c(1)=0

c(2)=0

c(3)=0

c(4)=0

c(5)=1

c(6)=npnow

c(7)=npnow

c(8)=2

isw=8

do i=1,npnow

isw=isw+1

c(isw)=xdatwk(i)

isw=isw+1

c(isw)=ydatwk(i)

enddo

ip=2

ir=1

do ig=1,ng

e1=eg(ig)

if (ig.eq.1) e1=0

e2=eg(ig+1)

if (ig.eq.ng) e2=ebig

call intega(ansf1(ig),e1,e2,c(1),ip,ir)

enddo

sump=zero

do ig=1,ng

sump=sump+ansf1(ig)

enddo

factn=1

if (sump.gt.zero) factn=1/sump

c

c     store final result to sed array

c

320 continue

do ig=1,ng

sed(ikt,ig)=sed(ikt,ig)+ansf1(ig)*pe*factn

enddo

c

return

end

*/

*/ Included in upn_Sublet

*/

*/  increase the allowed number of legendre terms in h6ddx

*/  to handle the new ENDF/B-VII mo95 evaluation.

*/

*/ *d up15.9

*/       dimension cnow(*),p(65)

*/ *d up30.10

*/ *i heatr.3298

*/       data nlmax/65/

*/

*/ Kazuaki Kosako, Shimizu Corporation

*/ kinematic method

*/

*i heatr.55

c     *    kkerma   0/1=total (mt301) is energy balance / kinematic    *

c     *             (default=0)                                        *

*i heatr.91

common/heat6/kkerma

*d heatr.139

kkerma=0

read(nsysi,*) matd,npk,nqa,ntemp,local,iprint,break,kkerma

*i heatr.151

if (kkerma.eq.1) then

if (npk.gt.0) then

mtkk=0

do i=1,npk

if (mtk(i).eq.443) mtkk=i

enddo

if (mtkk.eq.0) then

npk=npk+1

if (kchk.eq.1) then

npkk=3*npk+7

else

npkk=npk+3

endif

if (npkk.gt.npkmax) call error('heatr',

&           'requested too many kerma mt-s (6+mt301 allowed).',' ')

mtk(npk)=443

endif

else

npk=1

mtk(npk)=443

endif

endif

*i heatr.4997

common/heat6/kkerma

*i heatr.5045

if (kkerma.eq.1) then

do i=2,npk

if (mtp(i).eq.443) mtkk=i

enddo

endif

*i heatr.5121

if (mt.eq.301.and.kkerma.eq.1) a(ibase+i)=c(mtkk)

*i heatr.5146

if (kkerma.eq.1) write(nsyso,'(/'' total kerma (mt=301) was '',

&  ''replaced to kinematic kerma (mt=443).'')')

*/

## C.11 upn_Cabellos

REM upn_Cabellos : JEFF31 update

REM                -llf

*/ acer - O. Cabellos, NEA Data Bank Consultant, Sep-2005

*/ Error in acer for processing Al-27, Cl-35,I-129,Rh-103

*ident upNEA1

*d acer.4220

if (nethr.gt.1) call aordr(nethr,200,a(iethr))

*/

*/ Additional updates needed to process JEFF-3.1

*/

*/ Updates from Cabellos

*/

*ident upNEA2

*/ Error when processing Thermal Scattering for H-1(in H2O) at 293.6K (llf=0)

*/ Consultant: O. Cabellos, NEA Data Bank

*d broadr.503

*/       sf=slf+(tt(llf)-slf)*(enow-elast)/(tt(1)-elast)

if(llf.gt.0) then

sf=slf+(tt(llf)-slf)*(enow-elast)/(tt(1)-elast)

else

sf=slf

endif

*/

*d broadr.506

*/       sf=tt(llf)

if(llf.gt.0) sf=tt(llf)

*/

*/ ------------------------------------------------Sep05------end

## C.12 upn_Leichtle_Mod

REM upn_Leichtle_Mod : Be-9 and others (Li7)

REM                - Include: upac1, upac2 (with some modifications because it

REM                  corresponds with up57)

REM                - Do not include:

REM                  - upre1 (equivalent to up54)

REM                  - upac3 (equivalent to up57)

*/ UPN Leichtle + NEA update

*/

*ident upac1

*/ acer -- 05jun01

*/ corrections by I. Schmuck (FZK)

*/ some of them are redundant due to later up's; only nonredundant (till up50)

*/ are included in this upacer1

*/

*/ some error in subroutine acensd when processing d-Li evaluation by

*/ INPE Obninsk

*d acer.5621

if (mfh.eq.6 .and. law.eq.7.) then

*/ problem with amu=1 when processing d-Li evaluations

*i acer.5837

if (amu .eq. 1.) amu=0.999

*/ Equivalent to up54

*/ *ident upre1

*/ */ reconr -- 05jun01

*/ */ corrections by D. Leichtle, I. Schmuck (FZK)

*/ */ allow for processing of EFF3.0/NMOD=3 9Be with (n,2n) subsections in MT875-

*/ */ 890. reconr needs no know these MT-numbers.

*/ *d reconr.1696

*/          if (mth.ge.900) go to 150

*/

*/ Equivalent to up57

*ident upac2

*/ */ acer -- 05jun01

*/ */ corrections by D. Leichtle, I. Schmuck (FZK)

*/ */ allow for processing of EFF3.0/NMOD=3 9Be with (n,2n) subsections in MT875-

*/ */ 890.

*/ */

*/ */ mt up to 900 may be processed in unionx

*/ *d acer.1939

*/ */      &           (iverf.ge.6.and.mt.gt.900)) then

*/ */ temporary storage for unified grids used in multiple angular distributions

*i acer.4673

dimension etemp(200),amutmp(200)

*/ */ include mt>=875 in counting neutron emitting reactions

*/ *d acer.4759

*/                   if ((mt.ge.5.and.mt.le.91). or.

*/      &                (mt.ge.875 .and. mt.le.899)) then

*/ skip over mt92-849 for production of incident particle

*i acer.5021

if(mt.ge.92 .and. mt.le.849) iskip=1

*/ */ rewind file 3 to check all cross sections again

*/ *d acer.5118,5120

*/       call findf(matd,3,2,nin)

*/ */ neutron absorption for mt92-849, above 849 neutron emission possible

*/ *d acer.5127

*/             if (mt.gt.91 .and. mt.le.849) iskip=0

*/ get number of subsections in mf6

*i acer.5341

nk=a(iscr+4)

if (mf.eq.4) nk=0

*/ store pointer to yield-record and read it completely

*i acer.5370

iyield=iscr

iscr=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

iscr=iscr+nw

enddo

*/ store interpolation law for energies

*i acer.5374

ilne=nint(a(iscr+7))

*/ treat multiple neutron angular distributions (mf=6, law=7, newfor=1).

*/ find common energy and angular grids for all subsections.

*i acer.5410

ik=1

iik=0

mne=ne

if (mf.eq.6 .and. law.eq.7 .and. newfor.ne.0 .and.

&                      izai.eq.1) then

ine=ne

mne=ne

intne=1

inmu=nmu

mnmu=nmu

intnmu=1

do while (ik.lt.nk .and. awp.eq.1)

iik=iik+1

do iie=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

ein=sigfig(a(iscr+1),7,0)

if (law.eq.7.) nmu=nint(a(iscr+3))

m=nint(a(iscr+4))

n=nint(a(iscr+5))

jscr=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(jscr),nb,nw)

jscr=jscr+nw

enddo

c

c                          ***process mu-grid

do i=1,n

amuin=a(iscr+4+2*m+2*i)

if (ik.eq.1) then

amutmp(i)=amuin

else

i2=1

idone=0

do while(i2.le.mnmu .and. idone.eq.0)

if (amuin.lt.amutmp(i2)-0.001)

&                                 then

c

C                                      ***new angular grid point found

do j=mnmu,i2,-1

amutmp(j+1)=amutmp(j)

enddo

amutmp(i2)=amuin

mnmu=mnmu+1

idone=1

else if (amuin.lt.amutmp(i2)+0.001)

&                                 then

c

C                                       ***this angle already exists

idone=1

endif

i2=i2+1

enddo

endif

enddo

c

c                          ***process e-grid

if (ik.eq.1) then

etemp(iie)=ein

else

i2=1

idone=0

do while(i2.lt.mne .and. idone.eq.0)

if (ein.lt.etemp(i2)*0.9999) then

c

C                                   ***new energy grid point found

do j=mne,i2,-1

etemp(j+1)=etemp(j)

enddo

etemp(i2)=ein

mne=mne+1

idone=1

else if (ein.lt.etemp(i2)*1.0001) then

c

C                                   ***this energy already exists

idone=1

endif

i2=i2+1

enddo

endif

c

c                          ***skip energy distribution

do i=1,n

call tab1io(nin,0,0,a(iscr),nb,nw)

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

enddo

enddo

c

C                       ***proceed with next subsection

ik=ik+1

call tab1io(nin,0,0,a(iscr),nb,nw)

awp=c2h

if (awp.eq.1 .and. l2h.ne.law)

&                     call error('acelod',

&                     'different angular distributions laws',' ')

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

call tab2io(nin,0,0,a(iscr),nb,nw)

ne=nint(a(iscr+5))

enddo

c

c                    ***no energy interpolation needed?

if (mne.eq.ine) intne=0

c

c                    ***no angle interpolation needed?

if (mnmu.eq.inmu) intnmu=0

call findf(matd,mf,mt,nin)

call contio(nin,0,0,a(iscr),nb,mw)

call tab1io(nin,0,0,a(iscr),nb,nw)

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

call tab2io(nin,0,0,a(iscr),nb,nw)

ne=nint(a(iscr+5))

endif

*d acer.5411

xss(next)=mne

*d acer.5413,5414

il=ie+mne

next=il+mne+1

*/ process now multiple angular distributions (if actually found)

*d acer.5419,5420

if (iik.gt.1) then

c

c                       ***multiple angular distributions found

do i=1,ne

a(iscr+i-1)=etemp(i)

enddo

iegrid=iscr

iscr=iscr+ne

do i=1,mnmu

a(iscr+i-1)=amutmp(i)

enddo

imugrid=iscr

iscr=iscr+mnmu

call acend2(ir,next,iscr,nin,last,law,ne,ie,il,

&                  iso,iik,mne,mnmu,iyield,iegrid,imugrid,ilne,

&                  intne,intmu)

else

call acensd(ir,next,iscr,nin,awp,ltt3,lttn,

&                  ltt,last,law,ne,ie,il,iso)

endif

*/ subroutine acend2: combination of multiple angular distributions

*i acer.5749

subroutine acend2(ir,next,iscr,nin,last,law,ne,ie,il,iso,iik,

&  mne,mnmu,iyield,iegrid,imugrid,ilne,intne,intmu)

c     ******************************************************************

c     process this neutron scattering distribution.

c     ******************************************************************

*if sw

implicit real*8 (a-h,o-z)

*endif

integer esz,sig,and,tyr,dlw,gpd,fis,sigp,andp,dlwp,yp,end

common/jxst/esz,nu,mtr,lqr,tyr,lsig,sig,land,and,ldlw,dlw,

&  gpd,mtrp,lsigp,sigp,landp,andp,ldlwp,dlwp,yp,fis,end,

&  iurpt,jxsd(9)

common/lsize/max1,max2,max3

common/xsst/xss(4000000),n3 ! NEA changes

common/mainio/nsysi,nsyso,nsyse,ntty

common/cont/c1h,c2h,l1h,l2h,n1h,n2h,math,mfh,mth,nsh,nsp,nsc

common/astore/a(80000)

common/ace7/awi,izai,mcnpx,newfor

dimension xxmu(mnmu),xfmu(mnmu),x2fmu(mnmu)

external error,tab1io,listio,moreio,tab2io,findex

external pttab2,ptleg2,ptlegc

c NEA, 5-Oct-2005

external intega

c NEA, 5-Oct-2005

data emev/1.d6/

data etop/1.d10/

data rmin/1.d-30/

ik=1

next0=next

c

c     ***initialize xss-array

if (next+2+3*mnmu.gt.max3) call error('acend2',

&   'insufficient storage for angular distributions.',' ')

do i=0,(2+3*mnmu)*mne

xss(next+i)=0.0

enddo

c

c     ***loop over particle subsections

do while (ik.le.iik)

ieinold=1

next=next0

c

c        ***loop over incident energies

do j=1,ne

call tab1io(nin,0,0,a(iscr),nb,nw)

jscr=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(jscr),nb,nw)

jscr=jscr+nw

enddo

ein=sigfig(a(iscr+1),7,0)

ilnmu=nint(a(iscr+7))

c

c           ***find position of present energy in common grid

idone=0

ieinold=0

do while (ieinold.lt.mne .and. idone.eq.0)

ieinold=ieinold+1

if (abs(ein-a(iegrid+ieinold-1)).lt.ein/1000.) idone=1

enddo

next=next0+(2+3*mnmu)*(ieinold-1)

xss(next)=ilnmu

xss(next+1)=mnmu

lastfmu=next+1+mnmu

x1=-1

x2=1

c NEA, 5-Oct-2005

i_IP=2

i_IR=1

c           call intega(renorm,x1,x2,a(iscr),2,1)

call intega(renorm,x1,x2,a(iscr),i_IP,i_IR)

c NEA, 5-Oct-2005

c

c           ***transformation to unified angular grid, normalization,

c           ***put in temporary storage

do i=1,mnmu

xmu=a(imugrid+i-1)

c NEA, 5-Oct-2005

i_IP=2

i_IR=1

c              call terpa(fmu,xmu,xmu1,idis,a(iscr),2,1)

call terpa(fmu,xmu,xmu1,idis,a(iscr),i_IP,i_IR)

c NEA, 5-Oct-2005

xxmu(i)=xmu

xfmu(i)=fmu/renorm

enddo

c

c           ***check for energies not covered

if (j.gt.1) then

i=ieinold+1

einold=a(iegrid+ieinold-1)

do while (i.le.mne)

ei=a(iegrid+i-1)

if (ei.lt.ein) then

c

c                    ***set interpolation scheme (assume ilnmu)

next=next0+(2+3*mnmu)*(i-1)

xss(next)=ilnmu

xss(next+1)=mnmu

c NEA, 5-Oct-2005

i_IP=2

i_IR=1

c                  call terpa(yield,ei,xnext,idis,a(iyield),2,1)

call terpa(yield,ei,xnext,idis,a(iyield),i_IP,i_IR)

c NEA, 5-Oct-2005

c

c                    ***interpolate angular distribution to that energy

renorm=0.0

do k=1,mnmu

call terp1(einold,xss(lastfmu+k),ein,

&                             xfmu(k),ei,fmu,ilne)

xss(next+1+k)=sigfig(xxmu(k),7,0)

x2fmu(k)=fmu

renorm=renorm+fmu

enddo

do k=1,mnmu

x2fmu(k)=x2fmu(k)/renorm*yield

xss(next+1+mnmu+k)=xss(next+1+mnmu+k)+x2fmu(k)

enddo

i=i+1

else

i=mne+1

endif

enddo

endif

c

c           ***store and add now present distribution

c NEA, 5-Oct-2005

i_IP=2

i_IR=1

c           call terpa(yield,ein,xnext,idis,a(iyield),2,1)

call terpa(yield,ein,xnext,idis,a(iyield),i_IP,i_IR)

c NEA, 5-Oct-2005

next=next0+(2+3*mnmu)*(ieinold-1)

do i=1,mnmu

xss(next+1+i)=sigfig(xxmu(i),7,0)

xss(next+1+mnmu+i)=xss(next+1+mnmu+i)+xfmu(i)*yield

enddo

do i=1,mnmu

call tab1io(nin,0,0,a(iscr),nb,nw)

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

enddo

enddo

c

c        ***next incident energy

enddo

ik=ik+1

iyield=iscr

call tab1io(nin,0,0,a(iscr),nb,nw)

iscr=iscr+nw

do while (nb.ne.0)

call moreio(nin,0,0,a(iscr),nb,nw)

iscr=iscr+nw

enddo

call tab2io(nin,0,0,a(iscr),nb,nw)

ne=nint(a(iscr+5))

c

c     ***next particle subsection

enddo

c

c     ***do now final processing

next=next0

do j=1,mne

xss(ie+j)=sigfig(a(iegrid+j-1)/emev,7,0)

xss(il+j)=-(next-and+1)

do i=1,mnmu

xss(next+1+mnmu+i)=sigfig(xss(next+1+mnmu+i),7,0)

if (xss(next+1+mnmu+i).lt.rmin) xss(next+1+mnmu+i)=0

if (i.eq.1) then

xss(next+1+2*mnmu+i)=0

else

sum=xss(next+1+2*mnmu+i-1)+

&             gral(xss(next+1+i-1),xss(next+1+mnmu+i-1),

&                  xss(next+1+i),xss(next+1+mnmu+i),

&                  xss(next+1+i-1),xss(next+1+i),ilnmu)

xss(next+1+2*mnmu+i)=sigfig(sum,7,0)

endif

enddo

renorm=1/xss(next+1+3*mnmu)

do i=1,mnmu

xss(next+1+2*mnmu+i)=renorm*xss(next+1+2*mnmu+i)

xss(next+1+2*mnmu+i)=sigfig(xss(next+1+2*mnmu+i),9,0)

enddo

next=next+2+3*mnmu

enddo

iso=0

return

end

c

*/ read complete tab1-record

*i acer.9401

do while (nb.ne.0)

call moreio(nin,0,0,a(ll),nb,nw)

enddo

*/ Defined in up57

*/ */ set reaction name "MT" if out of defined region

*/ *d acer.11529

*/          if (i .gt. 408) then

*/             write(name,'(''MT'',i3)') mt

*/          else

*/             name=hndf(i)

*/          end if

*/

*/ Equivalent to up57

*/ *ident upac3

*/ */ acer -- 05jun01

*/ */ enlarge xss-array to fit the large ace-files. In addition, the output to

*/ */ xsdir has to be modified. cf up44

*/ *d up44.8

*/       max3=2000000

*/ *d up44.10

*/       common/xsst/xss(2000000),n3

*/ *d up44.12

*/       common/xsst/xss(2000000),n3

*/ *d up44.14

*/       common/xsst/xss(2000000),n3

*/ *d up44.16

*/       common/xsst/xss(2000000),n3

*/ *d up44.18

*/       common/xsst/xss(2000000),n3

*/ *d up44.20

*/       common/xsst/xss(2000000),n3

*/ *d up44.22

*/       common/xsst/xss(2000000),n3

*/ *d up44.24

*/       common/xsst/xss(2000000),n3

*/ *d up44.26

*/       common/xsst/xss(2000000),n3

*/ *d up44.28

*/       common/xsst/xss(2000000),n3

*/ *d up44.30

*/       common/xsst/xss(2000000),n3

*/ *d up44.32

*/       common/xsst/xss(2000000),n3

*/ *d up44.42

*/       common/xsst/xss(2000000),n3

*/ *d up44.44

*/       common/xsst/xss(2000000),n3

*/ *d up44.46

*/       common/xsst/xss(2000000),n3

*/ *d up44.48

*/       common/xsst/xss(2000000),n3

*/ *d up44.50

*/       common/xsst/xss(2000000),n3

*/ *d up44.52

*/       common/xsst/xss(2000000),n3

*/ *d up44.58

*/       common/xsst/xss(2000000),n3

*/ *d up44.60

*/       common/xsst/xss(2000000),n3

*/ *d up44.62

*/       common/xsst/xss(2000000),n3

*/ *d up44.68

*/       common/xsst/xss(2000000),n3

*/ *d up44.70

*/       common/xsst/xss(2000000),n3

*/ *d up44.72

*/       common/xsst/xss(2000000),n3

*/ *d up44.78

*/       common/xsst/xss(2000000),n3

*/ *d up44.80

*/       common/xsst/xss(2000000),n3

*/ *d up44.82

*/       common/xsst/xss(2000000),n3

*/ *d up44.88

*/       common/xsst/xss(2000000),n3

*/ *d up44.90

*/       common/xsst/xss(2000000),n3

*/ *d up44.92

*/       common/xsst/xss(2000000),n3

*/ *d up44.94

*/       common/xsst/xss(2000000),n3

*/ *d up44.96

*/       common/xsst/xss(2000000),n3

*/ *d up44.98

*/       common/xsst/xss(2000000),n3

*/ *d up44.100

*/       common/xsst/xss(2000000),n3

*/ *d up44.102

*/       common/xsst/xss(2000000),n3

*/ *d up44.104

*/       common/xsst/xss(2000000),n3

*/ *d up44.106

*/       common/xsst/xss(2000000),n3

*/

*/ Inlcuded in up57

*/ *ident up_NEA

*/*/ acer -- 05-Oct-20051

*/*/ bug in renorm

*/*d acer.9481

*/*/                            renorm=1/xss(next+3*npep)                    acer.9481

*/                              renorm=1.0

*/                              if(xss(next+3*npep).ne.0.0)

*/     &                        renorm=1/xss(next+3*npep)

*/*/

*/ bug for processing Li-7

*d acer.6917

*/                            renorm=1/xss(nexd+3*npep)                                acer.6917

renorm=1.0

if(xss(nexd+3*npep).ne.0.0)

&                        renorm=1/xss(nexd+3*npep)

## C.13 upn_Pescarini

REM upn_Pescarini: JEFF31 corrections.

REM              - Does not include updates equivalents to upfndl2, upki,

REM                up_thermr,nrg_re15

REM -----

*/ UPN Pescarini

*/

*/ Equivalent to fendl2 in upn_Trkov

*ident pesca

*/ */ --------- correction in gaspr (case Tc-99)

*/ *d gaspr.28

*/ */    dimension egas(50000),sgas(5,50000)

*/       dimension egas(60000),sgas(5,60000)

*/ *d gaspr.41

*/ */    maxg=50000

*/       maxg=60000

*/

*/ Equivalent to upki in upn_Hogenbirk

*/ */ --------- correction in heatr/h6ddx (case Mo-95)

*/ *d up30.10

*/ */    data nlmax/15/

*/       data nlmax/20/

*/ --------- correction in heatr/gambar (case Eu-151)

*d heatr.4845

*/    if (ehi.lt.e*(1-small).and.nne.lt.ne) go to 120

if (ehi.lt.e*(1+small).and.nne.lt.ne) go to 120

*/

*/ Equivalent to up_thermr in upn_Mattes

*/ -------- correction in thermr

*/ *d thermr.101

*/ */    dimension a(80000)

*/       dimension a(100000)

*/ *d thermr.131

*/ */    namax=80000

*/       namax=100000

*/ */  thermr/calcem

*/ -------- correction in thermr/coh (Be_TH,C_GPH cases)

*i thermr.782

if (enext.lt.e*(1+small)) go to 230

*/

*/ Equivalent to upn_Aldama

*/ */ corrections in thermr/calcem (H_H2O,D_D2O cases)

*/ *i thermr.1572

*/       loci=loc

*/       do while (nb.ne.0)

*/          loci=loci+nw

*/          call moreio(nendf,0,0,a(loci),nb,nw)

*/       enddo

*/ *i thermr.1598

*/       loci=loc

*/       do while (nb.ne.0)

*/          loci=loci+nw

*/          call moreio(nendf,0,0,a(loci),nb,nw)

*/       enddo

*/ -------- correction in purr/rdf3un (case Es-253)

*i purr.978

if (mth.eq.mtx(ix)) go to 130

*/

*/ Equivalent to nrg_re15 in Hogenbirk

*/ -------- corrections in reconr to prevent compiler warning

*/ */ correction in reconr/rdf2aa

*/ *i reconr.853

*/       zero=0.

*/ */ correction in reconr/rdf2hy

*/ *i reconr.937

*/       zero=0.

# APENDIX D. LANL Validation Suite

This Validation Suite is included in Reference [ICSBEP].

Most of them are not in electronic format, so a tedious hand-work has been performed to process these files.

## D.1 Jezebel: PU-MET-FAST-001

Bare Pu-239 Jezebel, ref. PU-MET-FAST-001

1    1    0.04029014 -1 imp:n=1

2    0     1  imp:n=0

1    so   6.3849

m1      94239.31c  3.7047E-02

94240.31c  1.7512E-03

94241.31c  1.1674E-04

31000.31c  1.3752E-03

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D.2 Jezebel-240: PU-MET-FAST-002

Bare Pu-240 Jezebel, ref. PU-MET-FAST-002

1    1    0.04055292 -1 imp:n=1

2    0     1  imp:n=0

1    so   6.6595

m1      94239.31c  2.9934E-02

94240.31c  7.8754E-03

94241.31c  1.2146E-03

94242.31c  1.5672E-04

31000.31c  1.3722E-03

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D3. Pu Buttons: PU-MET-FAST-003, case 103

PU-MET-UNMOD-HET-001 103.b <<Benchmark case>>

1 4 3.70511-02 -102 -5 u=2 imp:n=1 $ mocked-up shoe

2 0 102 -103 -1 u=2 imp:n=1 $ btm. spacer vd.

3 2 6.0263-02 102 -103 1 -2 u=2 imp:n=1 $ btm. spacer

4 0 102 -103 2 -5 u=2 imp:n=1 $ btm. spacer gap

c

10 2 2.8861-02 103 -104 -4 u=2 imp:n=1 $ PU#1 btm. Ht snk

11 3 8.4122-02 104 -105 -4 u=2 imp:n=1 $ PU#1 steel lid

12 1 4.9163-02 105 -106 -3 u=2 imp:n=1 $ PU#1 Pu core

13 2 6.0263-02 105 -106 3 -4 u=2 imp:n=1 $ PU#1 Al shell

14 2 6.0263-02 106 -107 -4 u=2 imp:n=1 $ PU#1 Al bottom

15 2 3.6744-02 107 -108 -4 u=2 imp:n=1 $ PU#1 top Ht snk

16 0 108 -109 -1 u=2 imp:n=1 $ PU#1/PU#2 spacer vd.

17 2 6.0263-02 108 -109 1 -2 u=2 imp:n=1 $ PU#1/PU#2 spacer

18 0 108 -109 2 -5 u=2 imp:n=1 $ PU#1/PU#2 spacer gap

19 0 103 -108 4 -5 u=2 imp:n=1 $ PU#1 gap

c

20 2 2.8861-02 109 -110 -4 u=2 imp:n=1 $ PU#2 btm. Ht snk

21 3 8.4122-02 110 -111 -4 u=2 imp:n=1 $ PU#2 steel lid

22 1 4.9163-02 111 -112 -3 u=2 imp:n=1 $ PU#2 Pu core

23 2 6.0263-02 111 -112 3 -4 u=2 imp:n=1 $ PU#2 Al shell

24 2 6.0263-02 112 -113 -4 u=2 imp:n=1 $ PU#2 Al bottom

25 2 3.6744-02 113 -114 -4 u=2 imp:n=1 $ PU#2 top Ht snk

26 0 114 -115 -1 u=2 imp:n=1 $ PU#2/PU#3 spacer vd.

27 2 6.0263-02 114 -115 1 -2 u=2 imp:n=1 $ PU#2/PU#3 spacer

28 0 114 -115 2 -5 u=2 imp:n=1 $ PU#2/PU#3 spacer gap

29 0 109 -114 4 -5 u=2 imp:n=1 $ PU#2 gap

c

30 2 2.8861-02 115 -116 -4 u=2 imp:n=1 $ PU#3 btm. Ht snk

31 3 8.4122-02 116 -117 -4 u=2 imp:n=1 $ PU#3 steel lid

32 1 4.9163-02 117 -118 -3 u=2 imp:n=1 $ PU#3 Pu core

33 2 6.0263-02 117 -118 3 -4 u=2 imp:n=1 $ PU#3 Al shell

34 2 6.0263-02 118 -119 -4 u=2 imp:n=1 $ PU#3 Al bottom

35 2 3.6744-02 119 -120 -4 u=2 imp:n=1 $ PU#3 top Ht snk

39 0 115 -120 4 -5 u=2 imp:n=1 $ PU#2 gap

40 0 120 -5 u=2 imp:n=1 $ vd. above sink

41 2 6.0263-02 5 u=2 imp:n=1 $ tube shell

c

140 0 -6 fill=2 u=1 imp:n=1 $ X+ Y+ tube

141 like 140 but trcl=( 0 9.60 0) imp:n=1 $ X+ Y- tube

142 like 140 but trcl=( 0 -9.60 0) imp:n=1 $ X- Y+ tube

143 like 140 but trcl=( 9.60 0 0) imp:n=1 $ X+ Y- tube

144 like 140 but trcl=( 9.60 9.60 0) imp:n=1 $ X- Y+ tube

145 like 140 but trcl=( 9.60 -9.60 0) imp:n=1 $ X+ Y- tube

146 like 140 but trcl=(-9.60 0 0) imp:n=1 $ X+ Y- tube

147 like 140 but trcl=(-9.60 9.60 0) imp:n=1 $ X- Y+ tube

148 like 140 but trcl=(-9.60 -9.60 0) imp:n=1 $ X+ Y- tube

150 0       #140 #141 #142 #143 #144

#145 #146 #147 #148 u=1 imp:n=1 $ on table-fuel

155 0 101 -121 150 -151 152 -153 fill=1 imp:n=1 $ rgn. abv. top

156 2 -2.376 100 -101 150 -151 152 -153 imp:n=1 $ Al tbl. top

157 3 5.8945-03 99 -100 150 -151 152 -153 imp:n=1 $ stl. tbl. prt

999 0 -99:121:-150:151:-152:153 imp:n=0 $ universe

1 cz 3.1040

2 cz 3.3260

3 cz 3.2625

4 cz 3.2995

5 cz 3.4250

6 cz 3.6090

99 pz -32.54

100 pz -2.54

101 pz 0.0

102 pz 8.30

103 pz 14.529

104 pz 15.164

105 pz 15.185

106 pz 19.818

107 pz 19.905

108 pz 20.384

109 pz 22.239

110 pz 22.874

111 pz 22.895

112 pz 27.528

113 pz 27.615

114 pz 28.094

115 pz 29.949

116 pz 30.584

117 pz 30.605

118 pz 35.238

119 pz 35.325

120 pz 35.804

121 pz 45.733

150 px -66.00

151 px 66.00

152 py -23.00

153 py 23.00

mode n

totnu

phys:n 30 1e-08

cut:n 1.0e16 0 -0.50 -0.25

print -10 -20 -30 -60 -85 -110 -120 -150 -170 -198

kcode 10000 1.0 50 550

sdef axs 0 0 1 ext d2 rad d1 pos d3

si1 3.2624

si2 2.3164

sp3 1 26r

si3 l 0.00 0.00 17.5015 0.00 9.60 17.5015

0.00 -9.60 17.5015

9.60 0.00 17.5015 9.60 9.60 17.5015

9.60 -9.60 17.5015

-9.60 0.00 17.5015 -9.60 9.60 17.5015

-9.60 -9.60 17.5015

0.00 0.00 25.2115 0.00 9.60 25.2115

0.00 -9.60 25.2115

9.60 0.00 25.2115 9.60 9.60 25.2115

9.60 -9.60 25.2115

-9.60 0.00 25.2115 -9.60 9.60 25.2115

-9.60 -9.60 25.2115

0.00 0.00 32.9215 0.00 9.60 32.9215

0.00 -9.60 32.9215

9.60 0.00 32.9215 9.60 9.60 32.9215

9.60 -9.60 32.9215

-9.60 0.00 32.9215 -9.60 9.60 32.9215

-9.60 -9.60 32.9215

m1      94239.31c  4.6010E-02

94240.31c  2.9236E-03

94241.31c  2.2433E-04

94242.31c  4.8566E-06

m2      13027.31c  1.0000E+00

m3    26054.31c   4.91693E-03

26056.31c   7.71853E-02

26057.31c   1.78255E-03

26058.31c   2.37224E-04

m4      13027.31c  2.9260E-02

26054.31c   4.55390E-04

26056.31c   7.14865E-03

26057.31c   1.65093E-04

26058.31c   2.19709E-05

## D4. Flattop-Pu : PU-MET-FAST-006

K-EFF CALCULATION FOR U(nat) REFLECTED PU SPHERE

1 1 0.04015889 -1    imp:n=1

2 2 0.048069744 1 -2 imp:n=1

3 0             2    imp:n=0

1 so 4.5332

2 so 24.142

m1      94239.31c  3.6697E-02

94240.31c  1.8700E-03

94241.31c  1.1639E-04

31000.31c  1.4755E-03

m2      92234.31c  2.6438E-06

92235.31c  3.4610E-04

92238.31c  4.7721E-02

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D5. THOR: PU-MET-FAST-008

Delta phase Pu sphere thorium reflector, Ref PU-MET-FAST-008

1    1    0.03945359 -1 imp:n=1

2    2    0.030054    1 -2 imp:n=1

3    0     2  imp:n=0

1    so    5.310

2    so    29.88

m1      94239.31c  3.6049E-02

94240.31c  1.9562E-03

94241.31c  1.1459E-04

31000.31c  1.3338E-03

m2      90232.31c  3.0054E-02

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D6. PU-MET-FAST-011

Water reflected alpha-phase Pu sphere, ref. PU-MET-FAST-011

1    1    0.049716393  -1 imp:n=1

2    2    0.100149      1 -2 imp:n=1

3    0     2  imp:n=0

1    so   4.1217

2    so   29.5217

m1      94239.31c  4.6982E-02

94240.31c  2.5753E-03

94241.31c  1.4915E-04

94242.31c  9.9432E-06

m2       1001.31c  6.6766E-02

8016.31c  3.3383E-02

mt2     lwtr01.31t

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D7. HISS/HPG : 	PU-COMP-INTER-001

HISS HPG Infinite Homogeneous Mixture ENDF/B-V

1 1 0.07534292 1 -2 3 -4 5 -6

2              0 -1:2:-3:4:-5:6

*1 px -1.0

*2 px 1.0

*3 py -1.0

*4 py 1.0

*5 pz -1.0

*6 pz 1.0

mode n

imp:n 1 0

kcode 5000 1.0 50 250

sdef cel=1 erg=d1 sur=0

sp1 -3

prdmp j 300

m1       1001.31c  1.0770E-04

5010.31c  1.0150E-04

5011.31c   4.086e-04

6000.31c  7.0900E-02

8016.31c  2.7070E-03

20040.31c   8.02671E-04

20042.31c   5.35716E-06

20043.31c   1.11780E-06

20044.31c   1.72721E-05

20046.31c   3.31200E-08

20048.31c   1.54836E-06

94239.31c  2.7350E-04

94240.31c  1.5490E-05

94241.31c  1.0720E-06

94242.31c  5.8000E-08

mt1  grph01.31t

totnu

print

## D8. PNL-2: PU-SOL-THERM-021, case 3

PS1288BY, 172.3 gPu/l,1.429g/cc, 4.9N,482.55gNO3/l,Bare Sph., 4.57% Pu240

C   Changed total atoms/cc from 9.92712-02 to 9.927121-02

1  0                5                    imp:n=0 $ Outside Everything

2  1  9.927121-02  -1   -3               imp:n=1 $ Pu(NO3)4 Solution

3  2  8.62396-02    1   -2  #6  #7       imp:n=1 $ SS347 Sphere

4  0                2    4  -5  #6 #7 #8 imp:n=1 $ Void Upper In. Hemisphere

5  0                2   -4  -5  #9 #10   imp:n=1 $ Void Lower In. Hemisphere

6  1  9.927121-02    1   -3   4  -7       imp:n=1 $ Liquid in Support Tube

7  0                3    4  -5  -7       imp:n=1 $ Air in Support Tube

8  2  8.62396-02    2    4  -5  -6   7   imp:n=1 $ SS347 Top Support Tube

9  0                2   -4  -5  -9       imp:n=1 $ Air in Bottom Tube

10  2  8.62396-02    2   -4  -5  -8   9   imp:n=1 $ SS347 Bottom Tube

1   so    19.3163           $ Sphere Inner Radius

2   so    19.4382           $ Sphere Outer Radius

3   px    19.3163           $ Liquid Level

4   px     0.0              $ Model Middle

5   so    49.4382           $ Outer Surface

6  c/x   0.0  3.811  2.8575 $ Top Support Tube OD

7  c/x   0.0  3.811  2.6924 $ Top Support Tube ID

8   cx     2.86             $ Bottom Tube OD

9   cx     2.555            $ Bottom Tube ID

mode n

kcode    10000 1.0   50  550

sdef pos 0.0 0.0 0.0 rad d1

sc1  Spherical Source about origin

si1    19.31

m1      94238.31c  2.6153E-08

94239.31c  4.1249E-04

94240.31c  2.0181E-05

94241.31c  1.2181E-06

94242.31c  3.8579E-08

7014.31c  4.6867E-03

1001.31c  5.4377E-02

8016.31c  3.9773E-02

m2    26054.31c   3.46930E-03

26056.31c   5.44606E-02

26057.31c   1.25773E-03

26058.31c   1.67381E-04

24050.31c   7.57247E-04

24052.31c   1.46027E-02

24053.31c   1.65583E-03

24054.31c   4.12172E-04

28058.31c   5.25575E-03

28060.31c   2.02449E-03

28061.31c   8.80114E-05

28062.31c   2.80556E-04

28064.31c   7.14900E-05

25055.31c  1.7363E-03

mt1  lwtr01.31t                           $S(Alpha,Beta)

totnu

prdmp

print    40 50 60 -175 -178

## D9. Jezebel-233:U233-MET-FAST-001

K-EFF CALCULATION FOR U-233 JEZEBEL

1    1     0.04760215 -1 imp:n=1

2    0     1             imp:n=0

1 so   5.9838

m1   92233.31c 4.6712-2 92234.31c 5.9026-4 92235.31c 1.4281-5

92238.31c 2.8561-4

kcode   5000 1.0 200 1200

ksrc    0. 0. 0.

print

## D10. Flattop-23: U233-MET-FAST-006

U-233 SPHERE Reflected by Normal Uranium

1    1     0.047591468 -1 imp:n=1

2    2     0.0480675    1 -2 imp:n=1

3    0     2  imp:n=0

1    so    4.2058

2    so    24.1194

m1   92233.31c 0.046710

92234.31c 0.00058772

92235.31c 0.000014158

92238.31c 0.00027959

m2   92235.31c 0.00035050

92238.31c 0.047717

kcode   5000  1.0 200 1200

ksrc    0. 0. 0.

print

## D11. U233-MF-05: U233-MET-FAST-005, case 2

U233 sphere Be reflector, Ref u233-met-fast-xxx

1    1     0.04816985  -1 imp:n=1

2    2     0.1212076    1 -2 imp:n=1

3    0     2  imp:n=0

1    so    4.5999

2    so    8.7960

m1   92233.31c 0.047312

92234.31c 0.00052770

92238.31c 0.00033015

m2   4009.31c  0.11983

8016.31c  0.0013776

mt2  beo01.31t

kcode   5000  1.0 200 1200

ksrc    0. 0. 0.

print

## D12. Falstaff-1: U233-SOL-INTER-001, case 1

FALSTAFF; Sol'n No. 1; Sphere No. 1; 8.00 cm Be

1 1 -1.9712 -1

2 2 -8.00    1 -2

3 3 -1.82    2 -3

4 0          3

1 so 7.8726

2 so 7.9209

3 so 15.9209

imp:n 1 1 1 0

m1   92232.31c 4.5608-8 92233.31c 2.2379-3 92234.31c 2.4316-5 &

92235.31c 8.9598-7 92238.31c 7.1284-6 1001.31c 5.5183-2 &

8016.31c 3.2043-2  9019.31c 4.7182-3

mt1  lwtr01.31t

m2   26054.31c 0.3552-2 26056.31c 5.6226-2 26057.31c 0.1286-2 &

26058.31c 0.0184-2 24050.31c 0.0726-2 24052.31c 1.3974-2 &

24053.31c 0.1584-2 24054.31c 0.0394-2 28058.31c 6.1623-3 &

28060.31c 2.3560-3 28061.31c 0.1020-3 28062.31c 0.3240-3 &

28064.31c 0.0821-3

m3   4009.31c 1.

mt3  bena01.31t

kcode 5000 1. 200 1200

ksrc 0. 0. 0.

## D13. SB-2½:U233-COMP-THERM-001, case 3

full LWBR SB-2.5 benchmark

c  rectangular array

c  U233, 340 UO2-ZrO2 seed rods (18x16)

c  no blanket

c

c  Cells

c  surface order:  pz1 ... cz1 ... (axial, then radial)

c  seed rod, infinitely long

11   5   4.3036-2    1     -21               u=1  imp:n=1  $ top zircaloy plug

12   1   8.0898-2    2  -1 -21               u=1  imp:n=1  $ 233UO2-ZrO2 seed

13   5   4.3036-2   -2 -21                   u=1  imp:n=1  $ bot.zircaloy plug

14   0                  21 -22               u=1  imp:n=1  $ void around meat

15   5   4.3036-2       22 -23               u=1  imp:n=1  $ zircaloy clad

16   6   1.0010-1           23               u=1  imp:n=1  $ surrounding water

31   0         -31 32 -33 34  lat=1  fill=1  u=3  imp:n=1  $ seed rod array

32   0         -99           trcl=1  fill=3  u=4  imp:n=1  $ c. seed rod array

75   0         -66 67 -68 69         fill=4  u=6  imp:n=1  $ cut arr. +-x, +-y

76   6   1.0010-1     66:-67:68:-69          u=6  imp:n=1  $ water around core

c  rod array with control blade bank

78  10  8.8821-2  -73 74 -76 75             u=13  imp:n=1  $ control blade a

79  10  8.8821-2  -73 74 -78 77             u=13  imp:n=1  $ control blade b

80  10  8.8821-2  -73 74 -79 80             u=13  imp:n=1  $ control blade c

81  10  8.8821-2  -73 74 -81 82             u=13  imp:n=1  $ control blade d

82   0         -5  #78 #79 #80 #81  fill=6  u=13  imp:n=1  $ core

83   6  1.0010-1    5  #78 #79 #80 #81      u=13  imp:n=1  $ water above core

c  rod without control blade bank

93   0             +6               fill=6  u=14  imp:n=1  $ core

96   6  1.0010-1   -6                       u=14  imp:n=1  $ water below core

c  put it all together

97   0             -91 12 -15       fill=13       imp:n=1  $

98   0             -91 16 -12       fill=14       imp:n=1  $

101  0              91:15:-16                     imp:n=0  $ outside

c

c  Surfaces

c  fixed elevations, pz, 0.00 = middle of fuel region

1   pz    19.05     $ fuel top (half of 15in fuel length)

2   pz   -19.05     $ fuel bottom

5   pz    25.8191   $ rod top (half of 20.83-.25in rod length)

6   pz   -25.8191   $ rod bottom

12  pz    16.05     $ control blade bank lower edge

15  pz    56.30     $ 1 ft above fuel

16  pz   -56.30     $ 1 ft below fuel

c  233U seed radial surfaces

21  cz     0.26797  $ 0.211in. OD Seed fuel pellet/zirc plug

22  cz     0.27940  $ 0.220in. ID Seed clad

23  cz     0.32385  $ 0.255in. OD Seed clad

c  seed rod window (square cell) surfaces

31  px     0.45974  $ pitch = 0.362in. = 0.91948cm

32  px    -0.45974

33  py     0.45974

34  py    -0.45974

c  core window (rectangular cell) surfaces

66  px     8.2753199   $ 9*pitch = 9*0.91948 - tad

67  px    -8.2753199

68  py     7.3558399   $ 8*pitch = 8*0.91948 - tad

69  py    -7.3558399

c  control blades

73  px     3.81     $ bank right edge (half of 3in. width)

74  px    -3.81     $ bank left edge (half of 3in. width)

75  py     5.42798  $ blade a inner edge (-12seedpitch + .5[.07in])

76  py     5.60578  $ blade a outer edge (-12seedpitch - .5[.07in])

77  py     1.75006  $ blade b inner edge (-4seedpitch + .5[.07in])

78  py     1.92786  $ blade b outer edge (-4seedpitch - .5[.07in])

79  py    -1.75006  $ blade c inner edge (-4seedpitch + .5[.07in])

80  py    -1.92786  $ blade c outer edge (-4seedpitch - .5[.07in])

81  py    -5.42798  $ blade d inner edge (-12seedpitch + .5[.07in])

82  py    -5.60578  $ blade d outer edge (-12seedpitch - .5[.07in])

c  model boundaries

91  cz    42.18     $ core + 1ft

99  cz   259.08     $ 17ft diameter containment tank (neglected)

c

c  Materials Data, Avogadro's number = 6.0221+23 particles/g-mole

m1   $ 233UO2-ZrO2 Seed, Ntot = 8.0898-2

8016.31c  5.3932E-02

40090.31c   1.17651E-02

40091.31c   2.56568E-03

40092.31c   3.92169E-03

40094.31c   3.97428E-03

40096.31c   6.40276E-04

92233.31c  3.9891E-03

92234.31c  6.3690E-05

92238.31c  4.5759E-05

m5   $ zircaloy-2 cladding plugs etc, Ntot=4.3036-2

40090.31c   2.18853E-02

40091.31c   4.77265E-03

40092.31c   7.29510E-03

40094.31c   7.39293E-03

40096.31c   1.19104E-03

50112.31c   4.84205E-06

50114.31c   3.24467E-06

50115.31c   1.69721E-06

50116.31c   7.25808E-05

50117.31c   3.83370E-05

50118.31c   1.20901E-04

50119.31c   4.28296E-05

50120.31c   1.62683E-04

50122.31c   2.31120E-05

50124.31c   2.89025E-05

m6   $ water, 0.9982 g/cc, Ntot=1.0010-1

1001.31c  6.6735E-02

8016.31c  3.3368E-02

mt6  lwtr01.31t

m10  $ borated SS control blades, Ntot=8.8821-2

26054.31c   3.46369E-03

26056.31c   5.43725E-02

26057.31c   1.25570E-03

26058.31c   1.67110E-04

5010.31c  3.7488E-03

24050.31c   7.57247E-04

24052.31c   1.46027E-02

24053.31c   1.65583E-03

24054.31c   4.12172E-04

25055.31c  8.6816E-04

28058.31c   5.11742E-03

28060.31c   1.97121E-03

28061.31c   8.56949E-05

28062.31c   2.73171E-04

28064.31c   6.96083E-05

c  translate coordinates to center core array

*tr1        -0.45974    0.45974     0.0     0 90 90     90 0 90    90 90 0   1

mode n

kcode       5000    1.0  200  1200

print

ksrc      0.5    -0.5     0          0.5    -7.75    0

0.5    -0.5    19          0.5    -7.75   19

0.5    -0.5   -19          0.5    -7.75  -19

0.5    -2.2     0          0.5    -5       0

2.2    -0.5     0          5      -0.5     0

2.2    -2.2     0          5      -5       0

7.75   -0.5     0          7.75   -7.75    0

7.75   -0.5    19          7.75   -7.75   19

7.75   -0.5   -19          7.75   -7.75  -19

9.75   -0.5     0

9.75   -0.5    19

9.75   -0.5   -19

-0.5    -0.5     0         -0.5    -7.75    0

-0.5    -0.5    19         -0.5    -7.75   19

-0.5    -0.5   -19         -0.5    -7.75  -19

-0.5    -2.2     0         -0.5    -5       0

-2.2    -0.5     0         -5      -0.5     0

-2.2    -2.2     0         -5      -5       0

-7.75   -0.5     0         -7.75   -7.75    0

-7.75   -0.5    19         -7.75   -7.75   19

-7.75   -0.5   -19         -7.75   -7.75  -19

-9.75   -0.5     0

-9.75   -0.5    19

-9.75   -0.5   -19

0.5     2.2     0          0.5     5       0

2.2     0.5     0          5       0.5     0

2.2     2.2     0          5       5       0

7.75    0.5     0          7.75    7.75    0

7.75    0.5    19          7.75    7.75   19

7.75    0.5   -19          7.75    7.75  -19

-0.5     2.2     0         -0.5     5       0

-2.2     0.5     0         -5       0.5     0

-2.2     2.2     0         -5       5       0

-7.75    0.5     0         -7.75    7.75    0

-7.75    0.5    19         -7.75    7.75   19

-7.75    0.5   -19         -7.75    7.75  -19

## D14. ORNL-11: U233-SOL-THERM-008

orl1 u233 expt 11 in nse

c

c cell cards

1 1 9.9935322e-02 -1

2 2 6.0274697e-02 -2 1

3 0                2

c surface cards

1 so 61.011

2 so 61.786

c importance card

imp:n 1.0 1.0 0.0

c material cards

m1      92233.31c  3.3441E-05

92234.31c  5.2503E-07

92235.31c  1.0184E-08

92238.31c  2.5474E-07

7014.31c  7.4943E-05

8016.31c  3.3469E-02

1001.31c  6.6357E-02

90232.31c  1.4756E-07

mt1    lwtr01.31t

c

c al 1100

c

m2      13027.31c  5.9881E-02

14028.31c   2.00969E-04

14029.31c   1.01759E-05

14030.31c   6.75490E-06

26054.31c   6.40495E-06

26056.31c   1.00544E-04

26057.31c   2.32200E-06

26058.31c   3.09016E-07

29063.31c   3.55285E-05

29065.31c   1.58355E-05

25055.31c  1.4853E-05

kcode 5000 1.0 200 1200

ksrc 0. 0. 0.

prdmp j 250

print

## D15. Godiva: HEU-MET-FAST-001

Godiva solid bare HEU sphere. CSB Data used. 05/12/93.

1 1 4.7984E-02 -1 imp:n=1

2 0 1 imp:n=0

1 so 8.7407

m1      92235.31c  4.4994E-02

92238.31c  2.4984E-03

92234.31c  4.9184E-04

kcode 5000 1.0 200 1200

ksrc 0. 0. 0.

print

## D16. Flattop-25: HEU-MET-FAST-028

K-EFF U(nat) REFLECTED HEU SPHERE

1 1 0.04767449 -1 imp:n=1

2 2 0.048069744 1 -2 imp:n=1

3 0 2 imp:n=0

1 so 6.1156

2 so 24.1242

m1      92234.31c  4.8869E-04

92235.31c  4.4482E-02

92238.31c  2.7038E-03

m2      92234.31c  2.6438E-06

92235.31c  3.4610E-04

92238.31c  4.7721E-02

kcode 5000 1.0 200 1200

ksrc 0 0 0

print

## D17. Godiver: HEU-MET-FAST-004

Idealized HEU sphere (97.675 w/o) in sphere of H2O TANS 27, 412 (11/77)

1 1 0.048143 -1 $ HEU sphere

2 2 0.10021 1 -2 $ water sphere

3 0 2

1 so 6.5537 $ radius of HEU sphere

2 so 33.471 $ radius of water sphere

mode n

kcode 10000 1.0 50 550

imp:n 1.0 1.0 0.0

sdef cel=1 erg=d1 rad=d2 pos=0.0 0.0 0.0

sp1    -3

si2    0.0 0.65537

sp2    -21 2

vol    1179.1 155891. 0.0

area   539.74 14078.

c HEU (97.675 w/o)

m1   92234.31c 0.011150

92235.31c 0.97694

92236.31c 0.0019919

92238.31c 0.0099250

c Water

m2   1001.31c 0.66667

8016.31c 0.33333

mt2  lwtr01.31t

totnu

prdmp j 110

print

end of input

## D18. Zeus-2: HEU-MET-INTER-006, case 2

ZEUS  9 Units, 6 C Plates/Unit  Final Benchmark Model  ENDF/B-VI.4+PT

c        Comet Hardware

1        2    0.059114     11  -12   47  -48              $ Platen

2        2    0.059114      9  -19   44  -45              $ Alignment Tube

c        Reflector Regions

3        4    0.082780      1   -4    5   -8   10  -41

49                           $ Below Top Reflector

4        4    0.082780      1   -4    5   -8   41  -42  $ Upper Reflector

5        4    0.082780      1   -4    5   -8   42  -43

#40                           $ Hollow Reflector

6        4    0.082780     12  -13   46  -48            $ Bottom Reflector

c        Column of Platters

7        3    0.085821     13  -14   46  -48            $ Unit 1, Lwr Gr

8        1    0.048176     14  -15   46  -48            $ Unit 1, Inner HEU

9        3    0.085821     15  -16   46  -48            $ Unit 1, Upr Gr

10       3    0.085821     16  -17   46  -48            $ Unit 2, Lwr Gr

11       1    0.048176     17  -18   46  -48            $ Unit 2, Inner HEU

12       3    0.085821     18  -19   46  -48            $ Unit 2, Upr Gr

13       3    0.085821     19  -20  -48                 $ Unit 3, Lwr

14       1    0.048176     20  -21  -48                 $ Unit 3, Inner HEU

15       3    0.085821     21  -22  -48                 $ Unit 3, Upr Gr

16       3    0.085821     22  -23  -48                 $ Unit 4, Lwr Gr

17       1    0.048176     23  -24  -48                 $ Unit 4, Inner HEU

18       3    0.085821     24  -25  -48                 $ Unit 4, Upr Gr

19       3    0.085821     25  -26  -48                 $ Unit 5, Lwr Gr

20       1    0.048176     26  -27  -48                 $ Unit 5, Inner HEU

21       3    0.085821     27  -28  -48                 $ Unit 5, Upr Gr

22       3    0.085821     28  -29  -48                 $ Unit 6, Lwr Gr

23       1    0.048176     29  -30  -48                 $ Unit 6, Inner HEU

24       3    0.085821     30  -31  -48                 $ Unit 6, Upr Gr

25       3    0.085821     31  -32  -48                 $ Unit 7, Lwr Gr

26       1    0.048176     32  -33  -48                 $ Unit 7, Inner HEU

27       3    0.085821     33  -34  -48                 $ Unit 7, Upr Gr

28       3    0.085821     34  -35  -48                 $ Unit 8, Lwr Gr

29       1    0.048176     35  -36  -48                 $ Unit 8, Inner HEU

30       3    0.085821     36  -37  -48                 $ Unit 8, Upr Gr

31       3    0.085821     37  -38  -48                 $ Unit 9, Lwr Gr

32       1    0.048176     38  -39  -48                 $ Unit 9, Inner HEU

33       3    0.085821     39  -40  -48                 $ Unit 9, Upr Gr

c        Internal Voids

34       0                 11  -12   45  -47            $ A-Tube - Platen Gap

35       0                 10  -11   45  -49            $ A-Tube - Refl Gap

36       0                  9  -19  -44                 $ Inside Alig. Tube

37       0                 12  -19   45  -46            $ Tube-Platter Gap

38       0                 11  -41   48  -49            $ Platter-Rfl Gap

39       0                 40  -41  -48                 $ Column-Upr Rfl Gap

40       0                  2   -3    6   -7   42  -43  $ Above Top Reflector

c        External Voids

41       0                 -1   10                      $ Left of Side Rfls

42       0                  4   10                      $ Right of Side Rfls

43       0                  1   -4   -5   10            $ Front of Side Rfls

44       0                  1   -4    8   10            $ Behind Side Rfls

45       0                  1   -4    5   -8   43       $ Above Side Reflect

46       0                -10   #2  #36                 $ Below Reflectors

1       px            -44.14520                         $ Left Rfl Edge

2       px            -27.94000                         $ Left Int Rfl Edge

3       px             27.94000                         $ Right Int Rfl Edge

4       px             44.14520                         $ Right Rfl Edge

5       py            -44.14520                         $ Front Rfl Edge

6       py            -27.94000                         $ Front Int Rfl Edge

7       py             27.94000                         $ Back Int Rfl Edge

8       py             44.14520                      $ Back Rfl Edge

9       pz             -5.79120                      $ Bottom of Align. Tube

10      pz              0.0                          $ Bottom of Reflectors

11      pz             26.78384                      $ Bottom of Platen

12      pz             30.59384                      $ Top of Platen

13      pz             45.02104                      $ Column Reflector

14      pz             48.04312                      $ 1st Unit: Lwr Gr

15      pz             48.34284                      $ 1st Unit: HEU

16      pz             51.36492                      $ 1st Unit: Upr Gr

17      pz             54.38700                      $ 2nd Unit: Lwr Gr

18      pz             54.68672                      $ 2nd Unit: HEU

19      pz             57.70880                      $ 2nd Unit: Upr Gr

20      pz             60.73088                      $ 3rd Unit: Lwr Gr

21      pz             61.03060                      $ 3rd Unit: HEU

22      pz             64.05268                      $ 3rd Unit: Upr Gr

23      pz             67.07476                      $ 4th Unit: Lwr Gr

24      pz             67.37448                      $ 4th Unit: HEU

25      pz             70.39656                      $ 4th Unit: Upr Gr

26      pz             73.41864                      $ 5th Unit: Lwr Gr

27      pz             73.71836                      $ 5th Unit: HEU

28      pz             76.74044                      $ 5th Unit: Upr Gr

29      pz             79.76252                      $ 6th Unit: Lwr Gr

30      pz             80.06224                      $ 6th Unit: HEU

31      pz             83.08432                      $ 6th Unit: Upr Gr

32      pz             86.10640                      $ 7th Unit: Lwr Gr

33      pz             86.40612                      $ 7th Unit: HEU

34      pz             89.42820                      $ 7th Unit: Upr Gr

35      pz             92.45028                      $ 8th Unit: Lwr Gr

36      pz             92.75000                      $ 8th Unit: HEU

37      pz             95.77208                      $ 8th Unit: Upr Gr

38      pz             98.79416                      $ 9th Unit: Lwr Gr

39      pz             99.09388                      $ 9th Unit: HEU

40      pz            102.11596                      $ 9th Unit: Upr Gr

41      pz            102.89540                      $ Top of Crnr Refls

42      pz            117.32260                      $ Top Reflector

43      pz            123.90120                      $ Top of Side Refls

44      cz              2.5400                       $ 1.0-in Radius

45      cz              3.1496                       $ 1.24-in. Radius

46      cz              3.1750                       $ 1.25-in. Radius

47      cz              4.7625                       $ 1.875-in. Radius

48      cz             26.6700                       $ Platter OR

49      cz             26.7970                       $ Corner Rfl IR

mode     n

kcode    10000    1.0     50    550

imp:n    1.0      39r   0.0     5r

ksrc       0.0  -15.0   48.17287        0.0   15.0   48.17287

-15.0    0.0   48.17287       15.0    0.0   48.17287

0.0  -15.0   54.52084        0.0   15.0   52.52084

-15.0    0.0   54.52084       15.0    0.0   52.52084

0.0  -15.0   61.15252        0.0   15.0   61.15252

-15.0    0.0   61.15252       15.0    0.0   61.15252

0.0  -15.0   67.51164        0.0   15.0   67.51164

-15.0    0.0   67.51164       15.0    0.0   67.51164

0.0  -15.0   73.85198        0.0   15.0   73.85198

-15.0    0.0   73.85198       15.0    0.0   73.85198

0.0  -15.0   80.19334        0.0   15.0   80.19334

-15.0    0.0   80.19334       15.0    0.0   80.19334

0.0  -15.0   86.53822        0.0   15.0   86.53822

-15.0    0.0   86.53822       15.0    0.0   86.53822

0.0  -15.0   92.87829        0.0   15.0   92.87829

-15.0    0.0   92.87829       15.0    0.0   92.87829

0.0  -15.0   99.21454        0.0   15.0   99.21454

-15.0    0.0   99.21454       15.0    0.0   99.21454

vol          8242.27     691.91

569966.67  112462.83   30739.30   31781.3

6657.37     660.26    6657.37

6657.37     660.26    6657.37

6753.08     669.75    6753.08

6753.08     669.75    6753.08

6753.08     669.75    6753.08

6753.08     669.75    6753.08

6753.08     669.75    6753.08

6753.08     669.75    6753.08

6753.08     669.75    6753.08

152.75   59587.30    1287.04      13.68

1623.64    1741.72   20542.20

0.0        5r

area        10939.29     367.61     367.61   10939.29

10939.29     367.61     367.61   10939.29

31.16   10630.76

2224.75    2203.42    2202.91

2202.91    2202.91    2202.91

2202.91    2202.91    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

2234.58    2234.58    2234.58

7795.19    7715.19    7795.19    1013.41

1256.63     540.92     114.01

12754.20   17324.60

c        Average HEU (93.22 wt.%)

m1      92234.31c  4.9576E-04

92235.31c  4.4941E-02

92236.31c  1.5931E-04

92238.31c  2.5799E-03

c        Aluminum 6061 (2.70 g/cc)

m2    12024.31c   5.21721E-04

12025.31c   6.60490E-05

12026.31c   7.27200E-05

13027.31c  5.7816E-02

14028.31c   3.16303E-04

14029.31c   1.60158E-05

14030.31c   1.06314E-05

22046.31c   2.07455E-06

22047.31c   1.87086E-06

22048.31c   1.85376E-05

22049.31c   1.36040E-06

22050.31c   1.30256E-06

24050.31c  3.3536E-06

24052.31c  6.4673E-05

24053.31c  7.3325E-06

24054.31c  1.8254E-06

25055.31c  2.1915E-05

26054.31c  5.9360E-06

26056.31c  9.2280E-05

26057.31c  2.1128E-06

26058.31c  2.8171E-07

29063.31c  4.8053E-05

29065.31c  2.1418E-05

c        Graphite (1.7117 g/cc)

m3       6000.31c  8.5821E-02

c        Pure Copper (Average:  8.7351 g/cc)

m4      29063.31c  5.7259E-02

29065.31c  2.5521E-02

mt3      grph01.31t

totnu

prdmp     j   1275

print

end of input

## D19. SB-5: U233-COMP-THERM-001, case 6

full LWBR SB-5 benchmark

c  hexagonal array

c  U235, 217 UO2-ZrO2 seed rods

c  ThO2 blanket rods

c

c  Cells

c  surface order:  pz1 ... cz1 ... (axial, then radial)

c  seed rod, infinitely long

11   5   4.3036-2    1     -21               u=1  imp:n=1  $ top zircaloy plug

12   2   8.2231-2    2  -1 -21               u=1  imp:n=1  $ 235UO2-ZrO2 seed

13   5   4.3036-2   -2 -21                   u=1  imp:n=1  $ bott. Zircal.plug

14   0                  21 -22               u=1  imp:n=1  $ void around meat

15   5   4.3036-2       22 -23               u=1  imp:n=1  $ zircaloy clad

16  12   1.1828-1  -200 201 23 -202          u=1  imp:n=1  $ poly ring

17   6   1.0010-1  -200 201 202              u=1  imp:n=1  $ water around ring

18   6   1.0010-1   200     23               u=1  imp:n=1  $ water above ring

19   6   1.0010-1  -201     23               u=1  imp:n=1  $ water below ring

21   6   1.0010-1      -99                   u=2  imp:n=1  $ water "rod"

c  blanket rod, infinitely long

51   5   4.3036-2    1     -41               u=9  imp:n=1  $ top zircaloy plug

52   3   6.4923-2    2  -1 -41               u=9  imp:n=1  $ ThO2 blanket

53   5   4.3036-2   -2 -41                   u=9  imp:n=1  $ bott. Zircal.plug

54   0                  41 -42               u=9  imp:n=1  $ void around meat

55   5   4.3036-2       42 -43               u=9  imp:n=1  $ zircaloy clad

56   6   1.0010-1           43               u=9  imp:n=1  $ surrounding water

c  core array

61   0        -52 55 -51 54 -56 53   lat=2   u=8  imp:n=1

fill=-24:24 -24:24 0:0

2 27R 2 16R 2  3R

2 26R  2 17R  2  3R

2 25R   2 18R   2  3R

2 24R    2 19R    2  3R

2 23R   9 20R       2  3R

2 22R   9 21R         2  3R

2 21R   9 22R           2  3R

2 20R   9 23R             2  3R

2 19R   9 24R               2  3R

2 18R   9 25R                 2  3R

2 17R   9 26R                   2  3R

2 16R   9 27R                     2  3R

2 15R   9 28R                       2  3R

2 14R   9 29R                         2  3R

2 13R   9 30R                           2  3R

2 12R   9 31R                             2  3R

2 11R   9 11R   1 1 1 1 1 1 1 1 1   9 11R   2  3R

2 10R   9 11R   1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  9R   9 11R   1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  8R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  7R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  6R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  5R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  4R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  3R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  4R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  5R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  6R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  7R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1 1   9 11R   2  8R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1 1   9 11R   2  9R

2  3R   9 11R   1 1 1 1 1 1 1 1 1 1   9 11R   2 10R

2  3R   9 11R   1 1 1 1 1 1 1 1 1   9 11R   2 11R

2  3R   9 31R                             2 12R

2  3R   9 30R                           2 13R

2  3R   9 29R                         2 14R

2  3R   9 28R                       2 15R

2  3R   9 27R                     2 16R

2  3R   9 26R                   2 17R

2  3R   9 25R                 2 18R

2  3R   9 24R               2 19R

2  3R   9 23R             2 20R

2  3R   9 22R           2 21R

2  3R   9 21R         2 22R

2  3R   9 20R       2 23R

2  3R    2 19R    2 24R

2  3R   2 18R   2 25R

2  3R  2 17R  2 26R

2  3R 2 16R 2 27R

75   0                 -69          fill=8  u=6   imp:n=1  $ cut array

76   6   1.0010-1       69                  u=6   imp:n=1  $ wat.outside core

c  rod array with control blade bank

78  10  8.8821-2  -73 74 -76 75             u=13  imp:n=1  $ control blade a

79  10  8.8821-2  -73 74 -78 77             u=13  imp:n=1  $ control blade b

80  10  8.8821-2  -73 74 -79 80             u=13  imp:n=1  $ control blade c

81  10  8.8821-2  -73 74 -81 82             u=13  imp:n=1  $ control blade d

82   0         -5  #78 #79 #80 #81  fill=6  u=13  imp:n=1  $ core

83   6  1.0010-1    5  #78 #79 #80 #81      u=13  imp:n=1  $ water above core

c  rod array without control blade bank

93   0             +6               fill=6  u=14  imp:n=1  $ core

96   6  1.0010-1   -6                       u=14  imp:n=1  $ water below core

c  put it all together

97   0             -91  12 -15   fill=13          imp:n=1  $

98   0             -91  16 -12   fill=14          imp:n=1  $

101  0              91:15:-16                     imp:n=0  $ outside

c

c  Surfaces

c  fixed elevations, pz, 0.00 = middle of fuel region

1   pz    19.05     $ fuel top (half of 15in fuel length)

2   pz   -19.05     $ fuel bottom

5   pz    25.8191   $ rod top (half of 20.83-.25in rod length)

6   pz   -25.8191   $ rod bott., bott. of bott. rod spac. plate,top base plate

12  pz    15.765    $ control blade bank lower edge

15  pz    56.30     $ 1 ft above fuel

16  pz   -56.30     $ 1 ft below fuel

200 pz     0.3175   $ poly ring top (1/8 in.)

201 pz    -0.3175   $ bottom of poly rings (1/8 in.)

202 cz     0.72517  $ assumed poly ring R (=blanket pitch/2)

c  235U seed radial surfaces

21  cz     0.26797  $ 0.211in. OD Seed fuel pellet/zirc plug

22  cz     0.27940  $ 0.220in. ID Seed clad

23  cz     0.32385  $ 0.255in. OD Seed clad

c  ThO2 Blanket radial surfaces

41  cz     0.62103  $ 0.489in. OD blanket pellet/zirc plug

42  cz     0.63373  $ 0.499in. ID blanket clad

43  cz     0.72390  $ 0.570in. OD blanket clad

c  blanket rod window (hex cell) surfaces

51  p   1  1.73205  0    1.45034  $ pitch = 0.571in. = 1.45034cm

52  px                   0.72517

53  p  -1  1.73205  0   -1.45034

54  p   1  1.73205  0   -1.45034

55  px                  -0.72517

56  p  -1  1.73205  0    1.45034

c  core window surfaces

69  cz    29.8     $ 20.5*pitch=29.7320 but round up

c  control blades

73  px     3.81     $ bank right edge (half of 3in. width)

74  px    -3.81     $ bank left edge (half of 3in. width)

75  py     5.42798  $ blade a inner edge (from core SB-2.5)

76  py     5.60578  $ blade a outer edge (from core SB-2.5)

77  py     1.75006  $ blade b inner edge (from core SB-2.5)

78  py     1.92786  $ blade b outer edge (from core SB-2.5)

79  py    -1.75006  $ blade c inner edge (from core SB-2.5)

80  py    -1.92786  $ blade c outer edge (from core SB-2.5)

81  py    -5.42798  $ blade d inner edge (from core SB-2.5)

82  py    -5.60578  $ blade d outer edge (from core SB-2.5)

c  model boundaries

91  cz    60.28     $ core + 1ft

99  cz   259.08     $ 17ft diameter containment tank (neglected)

c

c  Materials Data, Avogadro's number = 6.0221+23 particles/g-mole

m2   $ 235UO2-ZrO2 Seed, Ntot = 8.2231

8016.31c  5.4821E-02

40090.31c   1.19580E-02

40091.31c   2.60775E-03

40092.31c   3.98600E-03

40094.31c   4.03946E-03

40096.31c   6.50776E-04

92234.31c  3.7302E-05

92235.31c  3.8783E-03

92238.31c  2.5273E-04

m3   $ ThO2 blanket, Ntot = 6.4923-2

8016.31c  4.3282E-02

90232.31c  2.1641E-02

64152.31c   1.85214E-10

64154.31c   2.01883E-09

64155.31c   1.37058E-08

64156.31c   1.89567E-08

64157.31c   1.44930E-08

64158.31c   2.30036E-08

64160.31c   2.02439E-08

m5   $ zircaloy-2 cladding plugs etc, Ntot=4.3036-2

40090.31c   2.18853E-02

40091.31c   4.77265E-03

40092.31c   7.29510E-03

40094.31c   7.39293E-03

40096.31c   1.19104E-03

50112.31c   4.84205E-06

50114.31c   3.24467E-06

50115.31c   1.69721E-06

50116.31c   7.25808E-05

50117.31c   3.83370E-05

50118.31c   1.20901E-04

50119.31c   4.28296E-05

50120.31c   1.62683E-04

50122.31c   2.31120E-05

50124.31c   2.89025E-05

m6   $ water, 0.9982 g/cc, Ntot=1.0010-1

1001.31c  6.6735E-02

8016.31c  3.3368E-02

mt6  lwtr01.31t

m10  $ borated SS control blades, Ntot=8.8821-2

26054.31c   3.46369E-03

26056.31c   5.43725E-02

26057.31c   1.25570E-03

26058.31c   1.67110E-04

5010.31c  3.7488E-03

24050.31c   7.57247E-04

24052.31c   1.46027E-02

24053.31c   1.65583E-03

24054.31c   4.12172E-04

25055.31c  8.6816E-04

28058.31c   5.11742E-03

28060.31c   1.97121E-03

28061.31c   8.56949E-05

28062.31c   2.73171E-04

28064.31c   6.96083E-05

m12  $ polyethelene rings, Ntot=1.1828-1

1001.31c  7.8854E-02

6000.31c  3.9427E-02

mt12 poly01.31t

mode n

kcode      10000    1.0  50  350

print

ksrc      0    -0.1     0          0    -5       0

0    -0.1    19          0    -5      19

0    -0.1   -19          0    -5     -19

0    -7.5     0          0    -15      0

0    -7.5    19          0    -15     19

0    -7.5   -19          0    -15    -19

0    -25      0

0    -25     19

0    -25    -19

3     -2.5    0         -3     -2.5    0

5     -6.2    0         -5     -6.2    0

5     -6.2   19         -5     -6.2   19

5     -6.2  -19         -5     -6.2  -19

7.1    -.1     0        -7.1    -.1    0

7.1    -.1    19        -7.1    -.1   19

7.1    -.1   -19        -7.1    -.1  -19

7.1   -7.5     0        -7.1   -7.5    0

14.5  -15       0       -14.5  -15      0

14.5  -25       0       -14.5  -25      0

14.5  -25      19       -14.5  -25     19

14.5  -25     -19       -14.5  -25    -19

16      -.1     0       -16      -.1    0

29      -.1     0       -29      -.1    0

29      -.1    19       -29      -.1   19

29      -.1   -19       -29      -.1  -19

0     5       0

0     5      19

0     5     -19

0     15      0          0     25      0

0     15     19          0     25     19

0     15    -19          0     25    -19

3      2.5    0         -3      2.5    0

5      6.2    0         -5      6.2    0

5      6.2   19         -5      6.2   19

5      6.2  -19         -5      6.2  -19

7.1    7.5     0        -7.1    7.5    0

14.5   15       0       -14.5   15      0

14.5   25       0       -14.5   25      0

14.5   25      19       -14.5   25     19

14.5   25     -19       -14.5   25    -19

## D20. ORNL-10: HEU-SOL-THERM-032

or2511 u235 expt 10 in nse

c ICSBEP HEU-SOL-THERM-032 (ORNL-10) ENDF/B-VI.2

c

c cell cards

1 1 1.0016089e-01 -1

2 2 6.0274697e-02 -2 1

3 0 2

c surface cards

1 so 61.011

2 so 61.786

c importance card

imp:n 1.0 1.0 0.0

c material cards

m1      92233.31c  3.9124E-09

92234.31c  4.0905E-07

92235.31c  3.6157E-05

92236.31c  2.0858E-07

92238.31c  1.9878E-06

1001.31c  6.6409e-02

7014.31c  1.1212E-04

8016.31c  3.3601e-02

mt1 lwtr01.31t

c

c al 1100

c

m2      13027.31c  5.9881E-02

14028.31c   2.00969E-04

14029.31c   1.01759E-05

14030.31c   6.75490E-06

25055.31c  1.4853E-05

26054.31c  6.4652E-06

26056.31c  1.0051E-04

26057.31c  2.3012E-06

26058.31c  3.0682E-07

29063.31c  3.5529E-05

29065.31c  1.5836E-05

kcode 5000 1.0 200 1200

ksrc 0.0 0.0 0.0

prdmp j 250

print

## D21. IEU-MF-03: IEU-MET-FAST-003

IEU-MET-FAST-003 Layered Uranium Bare Sphere

C ENDF/B-V cross sections, W split by atomic abundance

C W-180 fraction added to w-182 because of cross sections

C Cell Cards

1 1 4.9881e-2 -1

2 2 4.8244e-2 1 -2

3 3 4.7972e-2 2 -3

4 4 4.7722e-2 3 -4

5 5 4.7964e-2 4 -5

6 6 4.7796e-2 5 -6

7 7 4.7702e-2 6 -7

8 8 4.6950e-2 7 -8

9 9 4.8536e-2 8 -9

10 10 4.9395e-2 9 -10

11 0 10

C Surface Cards

1 so 2.000

2 so 6.000

3 so 7.550

4 so 9.150

5 so 11.00

6 so 12.25

7 so 13.25

8 so 14.00

9 so 15.00

10 so 15.324

C Data Cards

imp:n 1 1 1 1 1 1 1 1 1 1 0

kcode 5000 1.0 200 1200

ksrc 0.0 0.0 0.0

prdmp 3j 1 j

m1      92234.31c  1.2743E-04

92235.31c  1.7093E-02

92238.31c  2.9308E-02

26054.31c   1.50292E-05

26056.31c   2.35927E-04

26057.31c   5.44859E-06

26058.31c   7.25107E-07

6000.31c  5.5181E-04

29063.31c   8.42698E-04

29065.31c   3.75602E-04

28058.31c   8.98004E-04

28060.31c   3.45908E-04

28061.31c   1.50377E-05

28062.31c   4.79361E-05

28064.31c   1.22149E-05

74182.31c  1.5874E-06

74183.31c  8.5799E-07

74184.31c  1.8445E-06

74186.31c  1.7184E-06

m2      92234.31c  1.5814E-04

92235.31c  1.7321E-02

92238.31c  2.9785E-02

26054.31c   9.39058E-06

26056.31c   1.47412E-04

26057.31c   3.40439E-06

26058.31c   4.53061E-07

6000.31c  4.6687E-04

29063.31c   1.12851E-04

29065.31c   5.02991E-05

28058.31c   1.20258E-04

28060.31c   4.63229E-05

28061.31c   2.01381E-06

28062.31c   6.41946E-06

28064.31c   1.63578E-06

74182.31c  3.2232E-06

74183.31c  1.7422E-06

74184.31c  3.7454E-06

74186.31c  3.4892E-06

m3      92234.31c  1.5677E-04

92235.31c  1.7194E-02

92238.31c  2.9508E-02

26054.31c   9.30875E-06

26056.31c   1.46127E-04

26057.31c   3.37472E-06

26058.31c   4.49113E-07

6000.31c  3.7026E-04

29063.31c   1.89802E-04

29065.31c   8.45975E-05

28058.31c   2.02257E-04

28060.31c   7.79085E-05

28061.31c   3.38694E-06

28062.31c   1.07966E-05

28064.31c   2.75115E-06

74182.31c  3.1955E-06

74183.31c  1.7272E-06

74184.31c  3.7132E-06

74186.31c  3.4592E-06

m4      92234.31c  1.5581E-04

92235.31c  1.7174E-02

92238.31c  2.9235E-02

26054.31c   9.25205E-06

26056.31c   1.45237E-04

26057.31c   3.35417E-06

26058.31c   4.46378E-07

6000.31c  5.5201E-04

29063.31c   1.44517E-04

29065.31c   6.44131E-05

28058.31c   1.53997E-04

28060.31c   5.93191E-05

28061.31c   2.57879E-06

28062.31c   8.22047E-06

28064.31c   2.09470E-06

74182.31c  3.1759E-06

74183.31c  1.7166E-06

74184.31c  3.6904E-06

74186.31c  3.4380E-06

m5      92234.31c  1.3256E-04

92235.31c  1.7141E-02

92238.31c  2.9417E-02

26054.31c   6.95789E-06

26056.31c   1.09224E-04

26057.31c   2.52246E-06

26058.31c   3.35693E-07

6000.31c  7.3802E-04

29063.31c   1.34349E-04

29065.31c   5.98811E-05

28058.31c   1.43166E-04

28060.31c   5.51470E-05

28061.31c   2.39742E-06

28062.31c   7.64230E-06

28064.31c   1.94738E-06

74182.31c  3.1847E-06

74183.31c  1.7213E-06

74184.31c  3.7006E-06

74186.31c  3.4474E-06

m6      92234.31c  1.6004E-04

92235.31c  1.7121E-02

92238.31c  2.9159E-02

26054.31c   5.76492E-06

26056.31c   9.04970E-05

26057.31c   2.08997E-06

26058.31c   2.78137E-07

6000.31c  5.5031E-04

29063.31c   2.32916E-04

29065.31c   1.03814E-04

28058.31c   2.48202E-04

28060.31c   9.56064E-05

28061.31c   4.15633E-06

28062.31c   1.32492E-05

28064.31c   3.37610E-06

74182.31c  1.5831E-06

74183.31c  8.5566E-07

74184.31c  1.8395E-06

74186.31c  1.7137E-06

m7      92234.31c  1.7235E-04

92235.31c  1.6958E-02

92238.31c  2.8806E-02

26054.31c   5.70513E-06

26056.31c   8.95583E-05

26057.31c   2.06829E-06

26058.31c   2.75252E-07

6000.31c  9.0767E-04

29063.31c   2.48555E-04

29065.31c   1.10785E-04

28058.31c   2.64867E-04

28060.31c   1.02026E-04

28061.31c   4.43540E-06

28062.31c   1.41388E-05

28064.31c   3.60279E-06

74182.31c  3.1334E-06

74183.31c  1.6936E-06

74184.31c  3.6410E-06

74186.31c  3.3920E-06

m8      92234.31c  1.4729E-04

92235.31c  1.6779E-02

92238.31c  2.8482E-02

26054.31c   5.63721E-06

26056.31c   8.84921E-05

26057.31c   2.04367E-06

26058.31c   2.71975E-07

6000.31c  6.2781E-04

29063.31c   2.69687E-04

29065.31c   1.20203E-04

28058.31c   2.87387E-04

28060.31c   1.10700E-04

28061.31c   4.81251E-06

28062.31c   1.53409E-05

28064.31c   3.90911E-06

74182.31c  1.5480E-06

74183.31c  8.3671E-07

74184.31c  1.7988E-06

74186.31c  1.6758E-06

m9      92234.31c  1.4996E-04

92235.31c  1.7018E-02

92238.31c  2.9013E-02

26054.31c   8.03571E-06

26056.31c   1.26143E-04

26057.31c   2.91320E-06

26058.31c   3.87694E-07

6000.31c  1.3697E-03

29063.31c   2.77766E-04

29065.31c   1.23804E-04

28058.31c   2.95992E-04

28060.31c   1.14015E-04

28061.31c   4.95661E-06

28062.31c   1.58003E-05

28064.31c   4.02616E-06

74182.31c  3.1522E-06

74183.31c  1.7037E-06

74184.31c  3.6628E-06

74186.31c  3.4123E-06

m10     92234.31c  1.3891E-04

92235.31c  1.6796E-02

92238.31c  2.8748E-02

26054.31c   4.53677E-06

26056.31c   7.12176E-05

26057.31c   1.64473E-06

26058.31c   2.18883E-07

6000.31c  6.3157E-04

29063.31c   9.95287E-04

29065.31c   4.43613E-04

28058.31c   1.06057E-03

28060.31c   4.08528E-04

28061.31c   1.77601E-05

28062.31c   5.66141E-05

28064.31c   1.44262E-05

74182.31c  1.5573E-06

74183.31c  8.4172E-07

74184.31c  1.8096E-06

74186.31c  1.6858E-06

## D22. BIG TEN: IEU-MET-FAST-007

Big Ten Detailed Benchmark IEU-MET-FAST-007

c

c cell cards

1 3 4.8195662E-02 103 -108 4 -3 imp:n=1 $p1 nat

2 1 4.8270100E-02 103 -108 5 -4 imp:n=1 $p2 (93)

3 3 4.8195662E-02 103 -108 6 -5 imp:n=1 $p3 nat

4 1 4.8270100E-02 103 -108 7 -6 imp:n=1 $p4 (93)

5 3 4.8195662E-02 103 -108 8 -7 imp:n=1 $p5 nat

6 1 4.8270100E-02 103 -108 9 -8 imp:n=1 $p6 (93)

7 3 4.8195662E-02 103 -108 10 -9 imp:n=1 $p7 nat

8 1 4.8270100E-02 103 -108 11 -10 imp:n=1 $p8 (93)

9 3 4.8195662E-02 103 -108 12 -11 imp:n=1 $p9 nat

10 1 4.8270100E-02 103 -108 13 -12 imp:n=1 $p10 (93)

11 0 103 -107 14 -13 imp:n=1 $p11 void

12 3 4.8195662E-02 107 -108 15 -13 imp:n=1 $p12 nat

13 1 4.8270100E-02 107 -108 16 -15 imp:n=1 $p13 (93)

14 4 4.7779014E-02 106 -108 18 -16 imp:n=1 $p14 dep

15 0 107 -108 19 -18 imp:n=1 $p15 void

16 1 4.8270100E-02 107 -108 20 -19 imp:n=1 $p16 (93)

17 3 4.8195662E-02 107 -108 21 -20 imp:n=1 $p17 nat

18 0 107 -108 22 -21 imp:n=1 $p18 void

19 3 4.8195662E-02 107 -108 23 -22 imp:n=1 $p19 nat

20 1 4.8270100E-02 107 -108 24 -23 imp:n=1 $p20 (93)

21 3 4.8195662E-02 107 -108 25 -24 imp:n=1 $p21 nat

22 0 107 -108 26 -25 imp:n=1 $p22 void

23 3 4.8195662E-02 107 -108 27 -26 imp:n=1 $p23 nat

24 1 4.8270100E-02 107 -108 28 -27 imp:n=1 $p24 (93)

25 3 4.8195662E-02 107 -108 29 -28 imp:n=1 $p25 nat

26 0 107 -108 30 -29 imp:n=1 $p26 void

27 3 4.8195662E-02 107 -108 31 -30 imp:n=1 $p27 nat

28 1 4.8270100E-02 107 -108 32 -31 imp:n=1 $p28 (93)

29 3 4.8195662E-02 107 -108 33 -32 imp:n=1 $p29 nat

30 0 107 -108 34 -33 imp:n=1 $p30 void

31 3 4.8195662E-02 107 -108 35 -34 imp:n=1 $p31 nat

32 1 4.8270100E-02 107 -108 36 -35 imp:n=1 $p32 (93)

33 3 4.8195662E-02 107 -108 37 -36 imp:n=1 $p33 nat

34 0 107 -108 38 -37 imp:n=1 $p34 void

35 3 4.8195662E-02 107 -108 39 -38 imp:n=1 $p35 nat

36 1 4.8270100E-02 107 -108 40 -39 imp:n=1 $p36 (93)

37 3 4.8195662E-02 107 -108 41 -40 imp:n=1 $p37 nat

38 0 107 -108 42 -41 imp:n=1 $p38 void

39 3 4.8195662E-02 107 -108 43 -42 imp:n=1 $p39 nat

40 1 4.8270100E-02 107 -108 44 -43 imp:n=1 $p40 (93)

41 3 4.8195662E-02 107 -108 45 -44 imp:n=1 $p41 nat

42 0 107 -108 46 -45 imp:n=1 $p42 void

43 3 4.8195662E-02 107 -108 47 -46 imp:n=1 $p43 nat

44 0 107 -108 48 -47 imp:n=1 $p44 void

45 1 4.8270100E-02 105 -108 49 -48 imp:n=1 $p45 (93)

46 3 4.8195662E-02 105 -108 50 -49 imp:n=1 $p46 nat

47 0 105 -108 51 -50 imp:n=1 $p47 void

48 3 4.8195662E-02 105 -108 52 -51 imp:n=1 $p48 nat

49 1 4.8270100E-02 105 -108 53 -52 imp:n=1 $p49 (93)

50 3 4.8195662E-02 105 -108 54 -53 imp:n=1 $p50 nat

51 0 105 -108 55 -54 imp:n=1 $p51 void

52 3 4.8195662E-02 105 -108 56 -55 imp:n=1 $p52 nat

53 1 4.8270100E-02 105 -108 57 -56 imp:n=1 $p53 (93)

54 3 4.8195662E-02 105 -108 58 -57 imp:n=1 $p54 nat

55 0 105 -108 59 -58 imp:n=1 $p55 void

56 3 4.8195662E-02 105 -108 60 -59 imp:n=1 $p56 nat

57 1 4.8270100E-02 105 -108 61 -60 imp:n=1 $p57 (93)

58 3 4.8195662E-02 105 -108 62 -61 imp:n=1 $p58 nat

59 0 105 -108 63 -62 imp:n=1 $p59 void

60 3 4.8195662E-02 105 -108 64 -63 imp:n=1 $p60 nat

61 1 4.8270100E-02 105 -108 65 -64 imp:n=1 $p61 (93)

62 3 4.8195662E-02 105 -108 66 -65 imp:n=1 $p62 nat

63 0 105 -108 67 -66 imp:n=1 $p63 void

64 3 4.8195662E-02 105 -108 68 -67 imp:n=1 $p64 nat

65 1 4.8270100E-02 105 -108 69 -68 imp:n=1 $p65 (93)

66 5 4.8086876E-02 105 -108 71 -69 imp:n=1 $p66 mix

67 0 100 -101 17 -1 imp:n=1 $CV void

68 7 8.7974300E-02 101 -102 17 -1 imp:n=1 $CL ss304

69 2 4.7609209E-02 -105 70 -48 imp:n=1 $C1 (10)

70 2 4.7609209E-02 -107 48 -18 imp:n=1 $C2 (10)

71 2 4.7609209E-02 -106 18 -17 imp:n=1 $C3 (10)

72 2 4.7609209E-02 103 -106 17 -16 imp:n=1 $C4 (10)

73 2 4.7609209E-02 103 -107 16 -14 imp:n=1 $C5 (10)

74 2 4.7609209E-02 -100 17 -1 imp:n=1 $C6 (10)

75 2 4.7609209E-02 102 -103 17 -3 imp:n=1 $C7 (10)

76 2 4.7609209E-02 102 -104 3 -2 imp:n=1 $C8 (10)

77 4 4.7779014E-02 -105 72 -70 imp:n=1 $R1 dep

78 4 4.7779014E-02 105 -108 72 -71 imp:n=1 $R2 dep

79 4 4.7779014E-02 108 -109 72 -1 112 115 118 121 124 127 imp:n=1 $R3 dep

80 4 4.7779014E-02 105 -108 3 -1 imp:n=1 $R4 dep

81 4 4.7779014E-02 102 -105 2 -1 imp:n=1 $R5 dep

82 4 4.7779014E-02 104 -105 3 -2 imp:n=1 $R6 dep

83 4 4.7779014E-02 -110 72 -1 imp:n=1 $rrod1 dep

84 0 110 -111 72 -1 imp:n=1 $rv1 void

85 6 8.7493450E-02 111 -112 72 -1 imp:n=1 $rl1 ss347

86 4 4.7779014E-02 -113 72 -1 imp:n=1 $rrod2 dep

87 0 113 -114 72 -1 imp:n=1 $rv2 void

88 6 8.7493450E-02 114 -115 72 -1 imp:n=1 $rl2 ss347

89 4 4.7779014E-02 -116 72 -1 imp:n=1 $rrod3 dep

90 0 116 -117 72 -1 imp:n=1 $rv3 void

91 6 8.7493450E-02 117 -118 72 -1 imp:n=1 $rl3 ss347

92 4 4.7779014E-02 -119 72 -1 imp:n=1 $rrod4 dep

93 0 119 -120 72 -1 imp:n=1 $rv4 void

94 6 8.7493450E-02 120 -121 72 -1 imp:n=1 $rl4 ss347

95 4 4.7779014E-02 -122 72 -1 imp:n=1 $rrod5 dep

96 0 122 -123 72 -1 imp:n=1 $rv5 void

97 6 8.7493450E-02 123 -124 72 -1 imp:n=1 $rl5 ss347

98 4 4.7779014E-02 -125 72 -1 imp:n=1 $rrod6 dep

99 0 125 -126 72 -1 imp:n=1 $rv6 void

100 6 8.7493450E-02 126 -127 72 -1 imp:n=1 $rl6 ss347

101 0 (109:-72:1) imp:n=0

c surface cards

1 pz 39.05250 $top of C6, CV CL R5 R4 R3

2 pz 25.71750 $top of C8 R6

3 pz 23.81250 $top of P1 C7

4 pz 16.66240 $top of P2

5 pz 16.36268 $top of P3

6 pz 13.66012 $top of P4

7 pz 13.36040 $top of P5

8 pz 10.65784 $top of P6

9 pz 10.35812 $top of P7

10 pz 7.65556 $top of P8

11 pz 7.35584 $top of P9

12 pz 4.65328 $top of P10

13 pz 4.35356 $top of P11 and P12

14 pz 4.35102 $top of C5

15 pz 1.65100 $top of P13

16 pz 1.35128 $top of P14 C4

17 pz 0.00000 $top of C3

18 pz -1.35128 $top of P15 C2

19 pz -1.35382 $top of P16

20 pz -1.65354 $top of P17

21 pz -3.15468 $top of P18

22 pz -3.15722 $top of P19

23 pz -4.35864 $top of P20

24 pz -4.65836 $top of P21

25 pz -6.15950 $top of P22

26 pz -6.16204 $top of P23

27 pz -7.36346 $top of P24

28 pz -7.66318 $top of P25

29 pz -9.16432 $top of P26

30 pz -9.16686 $top of P27

31 pz -10.36828 $top of P28

32 pz -10.66800 $top of P29

33 pz -12.16914 $top of P30

34 pz -12.17168 $top of P31

35 pz -13.37310 $top of P32

36 pz -13.67282 $top of P33

37 pz -15.17396 $top of P34

38 pz -15.17650 $top of P35

39 pz -16.37792 $top of P36

40 pz -16.67764 $top of P37

41 pz -18.17878 $top of P38

42 pz -18.18132 $top of P39

43 pz -19.38274 $top of P40

44 pz -19.68246 $top of P41

45 pz -21.18360 $top of P42

46 pz -21.18614 $top of P43

47 pz -22.38756 $top of P44

48 pz -22.39010 $top of P45 C1

49 pz -22.68982 $top of P46

50 pz -24.19096 $top of P47

51 pz -24.19350 $top of P48

52 pz -25.39492 $top of P49

53 pz -25.69464 $top of P50

54 pz -27.19578 $top of P51

55 pz -27.19832 $top of P52

56 pz -28.39974 $top of P53

57 pz -28.69946 $top of P54

58 pz -30.20060 $top of P55

59 pz -30.20314 $top of P56

60 pz -31.40456 $top of P57

61 pz -31.70428 $top of P58

62 pz -33.20542 $top of P59

63 pz -33.20796 $top of P60

64 pz -34.40938 $top of P61

65 pz -34.70910 $top of P62

66 pz -36.21024 $top of P63

67 pz -36.21278 $top of P64

68 pz -37.41420 $top of P65

69 pz -37.71392 $top of P66

70 pz -41.73361 $top of R1

71 pz -42.22750 $bot of P66 top of R2

72 pz -57.46750 $bottom of R1 R2 R3

100 cz 1.79451 $o.r. C6 i.r. CV

101 cz 1.81610 $o.r. cv i.r. CL

102 cz 1.90500 $o.r. Cl i.r. C7, C8, R5

103 cz 3.17500 $o.r. c7 i.r. C4, C5, P1-P11

104 cz 4.28625 $o.r. c8 i.r. R6

105 cz 7.62000 $o.r. C1, R1, R5, R6 i.r. P45 - P66, R2, R4

106 cz 11.11250 $o.r. c3, c4 i.r. P14

107 cz 12.70000 $o.r. C2, C5, P11 i.r. P12, P13, P15-P44

108 cz 26.67000 $o.r. R2, R4, P1-66 i.r. R3

109 cz 41.91000 $o.r. R3

110 c/z 0.00000 -33.49752 4.43865 $o.r. rrod1

111 c/z 0.00000 -33.49752 4.52501 $o.r. rv1

112 c/z 0.00000 -33.49752 4.60375 $o.r. rl1

113 c/z -29.00970 -16.74876 4.43865 $o.r.1 rrod2

114 c/z -29.00970 -16.74876 4.52501 $o.r.1 rv2

115 c/z -29.00970 -16.74876 4.60375 $o.r.1 rl2

116 c/z 29.00970 -16.74876 4.43865 $o.r.1 rrod3

117 c/z 29.00970 -16.74876 4.52501 $o.r.1 rv3

118 c/z 29.00970 -16.74876 4.60375 $o.r.1 rl3

119 c/z -29.00970 16.74876 4.43865 $o.r.1 rrod4

120 c/z -29.00970 16.74876 4.52501 $o.r.1 rv4

121 c/z -29.00970 16.74876 4.60375 $o.r.1 rl4

122 c/z 29.00970 16.74876 4.43865 $o.r.1 rrod5

123 c/z 29.00970 16.74876 4.52501 $o.r.1 rv5

124 c/z 29.00970 16.74876 4.60375 $o.r.1 rl5

125 c/z 0.00000 33.49752 4.43865 $o.r. rrod6

126 c/z 0.00000 33.49752 4.52501 $o.r. rv6

127 c/z 0.00000 33.49752 4.60375 $o.r. rl6

c material cards

m1   $ U(93)

92234.31c  4.9814E-04

92235.31c  4.5034E-02

92236.31c  1.3236E-04

92238.31c  2.6056E-03

m2   $ U(10)

92234.31c  2.4761E-05

92235.31c  4.8461E-03

92236.31c  4.3348E-05

92238.31c  4.2695E-02

m3   $ U(nat)

92234.31c  2.6518E-06

92235.31c  3.4701E-04

92238.31c  4.7846E-02

m4   $ U(dep)

92234.31c  2.8672E-07

92235.31c  1.0058E-04

92236.31c  1.1468E-06

92238.31c  4.7677E-02

m5   $ P66

92234.31c  2.6458E-06

92235.31c  3.4623E-04

92238.31c  4.7738E-02

m6   $ steel 347

14028.31c   1.58211E-03

14029.31c   8.01092E-05

14030.31c   5.31774E-05

24050.31c   7.24659E-04

24052.31c   1.39743E-02

24053.31c   1.58458E-03

24054.31c   3.94435E-04

25055.31c  1.7539E-03

26054.31c   3.37829E-03

26056.31c   5.30320E-02

26057.31c   1.22474E-03

26058.31c   1.62990E-04

28058.31c   6.14708E-03

28060.31c   2.36783E-03

28061.31c   1.02937E-04

28062.31c   3.28136E-04

28064.31c   8.36141E-05

41093.31c  5.1855E-04

m7   $ steel 304

14028.31c   1.58211E-03

14029.31c   8.01092E-05

14030.31c   5.31774E-05

24050.31c   7.64894E-04

24052.31c   1.47502E-02

24053.31c   1.67256E-03

24054.31c   4.16335E-04

25055.31c  1.7539E-03

26054.31c   3.46655E-03

26056.31c   5.44175E-02

26057.31c   1.25674E-03

26058.31c   1.67249E-04

28058.31c   5.16909E-03

28060.31c   1.99111E-03

28061.31c   8.65602E-05

28062.31c   2.75930E-04

28064.31c   7.03112E-05

kcode 5000 1.00 200 1200

prdmp j -60 j 2

ksrc   .1 0. -39.6 .1 0. -33.5 .1 0. -27.0 .1 0. -21.0 .1 0. -15.0

.1 0. -9.0 .1 0. -3.0 .1 0. -0.68 .1 0. 6.0 .1 0. 15.

.1 0. 32.3

7.1 .1 0.68 .1 7.1 0.68 -7.1 .1 0.68 .1 -7.1 0.68

8.5 .1 2.85 .1 8.5 2.85 -8.5 .1 2.85 .1 -8.5 2.85

2.5 .1 9.00 .1 2.5 9.00 -2.5 .1 9.00 .1 -2.5 9.00

2.5 .1 20.2 .1 2.5 20.2 -2.5 .1 20.2 .1 -2.5 20.2

3.1 .1 24.8 .1 3.1 24.8 -3.1 .1 24.8 .1 -3.1 24.8

17.1 .1 -37.6 .1 17.1 -37.6 -17.1 .1 -37.6 .1 -17.1 -37.6

17.1 .1 -34.6 .1 17.1 -34.6 -17.1 .1 -34.6 .1 -17.1 -34.6

17.1 .1 -32.5 .1 17.1 -32.5 -17.1 .1 -32.5 .1 -17.1 -32.5

17.1 .1 -28.6 .1 17.1 -28.6 -17.1 .1 -28.6 .1 -17.1 -28.6

17.1 .1 -25.5 .1 17.1 -25.5 -17.1 .1 -25.5 .1 -17.1 -25.5

17.1 .1 -22.5 .1 17.1 -22.5 -17.1 .1 -22.5 .1 -17.1 -22.5

19.7 .1 -19.5 .1 19.7 -19.5 -19.7 .1 -19.5 .1 -19.7 -19.5

19.7 .1 -16.5 .1 19.7 -16.5 -19.7 .1 -16.5 .1 -19.7 -16.5

19.7 .1 -13.5 .1 19.7 -13.5 -19.7 .1 -13.5 .1 -19.7 -13.5

19.7 .1 -10.5 .1 19.7 -10.5 -19.7 .1 -10.5 .1 -19.7 -10.5

19.7 .1 -7.5 .1 19.7 -7.5 -19.7 .1 -7.5 .1 -19.7 -7.5

19.7 .1 -4.5 .1 19.7 -4.5 -19.7 .1 -4.5 .1 -19.7 -4.5

19.7 .1 -1.5 .1 19.7 -1.5 -19.7 .1 -1.5 .1 -19.7 -1.5

19.7 .1 1.5 .1 19.7 1.5 -19.7 .1 1.5 .1 -19.7 1.5

14.9 .1 4.5 .1 14.9 4.5 -14.9 .1 4.5 .1 -14.9 4.5

14.9 .1 7.5 .1 14.9 7.5 -14.9 .1 7.5 .1 -14.9 7.5

14.9 .1 10.5 .1 14.9 10.5 -14.9 .1 10.5 .1 -14.9 10.5

14.9 .1 13.5 .1 14.9 13.5 -14.9 .1 13.5 .1 -14.9 13.5

14.9 .1 16.5

## D23. IEU-MF-04: IEU-MET-FAST-004

IEU-MET-FAST-004 Layered Uranium Sphere, Graphite Reflected

C ENDF/B-V cross sections, W split by atomic abundance

C W-180 fraction added to W-182 because of cross sections

C Graphite thermal S(alpha,beta) treatment applied at 300K

C Cell Cards

1 0 -1

2 1 4.8243e-2 1 -2

3 2 4.8009e-2 2 -3

4 3 4.7960e-2 3 -4

5 4 4.8156e-2 4 -5

6 5 4.7909e-2 5 -6

7 6 4.7973e-2 6 -7

8 7 4.7478e-2 7 -8

9 8 7.7716e-2 8 -9

10 0 9

C Surface Cards

1 so 2.788

2 so 6.000

3 so 7.550

4 so 9.150

5 so 11.00

6 so 12.25

7 so 13.25

8 so 14.00

9 so 17.2

C Data Cards

imp:n 1 1 1 1 1 1 1 1 1 0

kcode 5000 1.0 200 1200

ksrc 5 0 0

prdmp j 350 j 1

C Material Cards

m1      92234.31c  1.5926E-04

92235.31c  1.7443E-02

92238.31c  2.9996E-02

26054.31c   9.45721E-06

26056.31c   1.48458E-04

26057.31c   3.42854E-06

26058.31c   4.56276E-07

6000.31c  4.7018E-04

74182.31c  3.2462E-06

74183.31c  1.7546E-06

74184.31c  3.7721E-06

74186.31c  3.5141E-06

m2      92234.31c  1.5878E-04

92235.31c  1.7415E-02

92238.31c  2.9887E-02

26054.31c   9.42857E-06

26056.31c   1.48008E-04

26057.31c   3.41816E-06

26058.31c   4.54894E-07

6000.31c  3.7502E-04

74182.31c  3.2365E-06

74183.31c  1.7493E-06

74184.31c  3.7608E-06

74186.31c  3.5035E-06

m3      92234.31c  1.5803E-04

92235.31c  1.7418E-02

92238.31c  2.9651E-02

26054.31c   9.38356E-06

26056.31c   1.47302E-04

26057.31c   3.40184E-06

26058.31c   4.52723E-07

6000.31c  5.5986E-04

74182.31c  3.2211E-06

74183.31c  1.7410E-06

74184.31c  3.7429E-06

74186.31c  3.4869E-06

m4      92234.31c  1.3423E-04

92235.31c  1.7356E-02

92238.31c  2.9786E-02

26054.31c   7.04556E-06

26056.31c   1.10600E-04

26057.31c   2.55424E-06

26058.31c   3.39923E-07

6000.31c  7.4727E-04

74182.31c  3.2246E-06

74183.31c  1.7429E-06

74184.31c  3.7469E-06

74186.31c  3.4906E-06

m5      92234.31c  1.6281E-04

92235.31c  1.7417E-02

92238.31c  2.9663E-02

26054.31c   5.86487E-06

26056.31c   9.20660E-05

26057.31c   2.12620E-06

26058.31c   2.82959E-07

6000.31c  5.5983E-04

74182.31c  1.6105E-06

74183.31c  8.7045E-07

74184.31c  1.8713E-06

74186.31c  1.7433E-06

m6      92234.31c  1.7609E-04

92235.31c  1.7326E-02

92238.31c  2.9432E-02

26054.31c   5.82893E-06

26056.31c   9.15017E-05

26057.31c   2.11317E-06

26058.31c   2.81225E-07

6000.31c  9.2737E-04

74182.31c  3.2013E-06

74183.31c  1.7303E-06

74184.31c  3.7199E-06

74186.31c  3.4655E-06

m7      92234.31c  1.5156E-04

92235.31c  1.7266E-02

92238.31c  2.9309E-02

26054.31c   5.80087E-06

26056.31c   9.10613E-05

26057.31c   2.10300E-06

26058.31c   2.79871E-07

6000.31c  6.4604E-04

74182.31c  1.5930E-06

74183.31c  8.6100E-07

74184.31c  1.8510E-06

74186.31c  1.7244E-06

m8       6000.31c  7.7716E-02

mt8   grph01.31t

## D24. Zebra-8H: MIX-MET-FAST-008, case 7

ZEBRA 8H

c U nat

41 1 4.713345E-02 1 -2 -103 104 -203 204 imp:n=1

c U enriched

42 2 4.740186E-02 2 -3 -103 104 -203 204 imp:n=1

c U nat

43 1 4.713345E-02 3 -4 -103 104 -203 204 imp:n=1

c void

3 0 1 -4 -105 106 -205 206 (103:-104:203:-204) imp:n=1

c Sheath

4 3 8.567983E-02 1 -4 -107 108 -207 208 (105:-106:205:-206) imp:n=1

c supercell

5 0 -1:4:107:-108:207:-208 imp:n=0

1 -4 pz 0

2 pz 0.9525

3 pz 1.27

4 -1 pz 2.2225

c

103 px 2.5335 $ Can and other pellets

104 px -2.5335 $ Can and other pellets

105 px 2.5510 $ Air gap

106 px -2.5510 $ Air gap

107 -108 px 2.6272 $ Sheath

108 -107 px -2.6272 $ Sheath

c

203 py 2.5335 $ Can and other pellets

204 py -2.5335 $ Can and other pellets

205 py 2.5510 $ Air gap

206 py -2.5510 $ Air gap

*207 py 2.6272 $ Sheath

*208 py -2.6272 $ Sheath

m1      92235.31c  3.3316E-04

92238.31c  4.5948E-02

6000.31c  4.9205E-04

26054.31c   6.18576E-06

26056.31c   9.71033E-05

26057.31c   2.24254E-06

26058.31c   2.98441E-07

14028.31c   1.94080E-04

14029.31c   9.82708E-06

14030.31c   6.52333E-06

1001.31c  4.3978E-05

m2      92235.31c  1.7730E-02

92238.31c  2.8957E-02

6000.31c  1.8452E-04

26054.31c   3.47935E-06

26056.31c   5.46184E-05

26057.31c   1.26138E-06

26058.31c   1.67866E-07

13027.31c  4.1070E-05

14028.31c   3.63903E-05

14029.31c   1.84260E-06

14030.31c   1.22314E-06

1001.31c  4.3978E-05

8016.31c  3.4631E-04

m3       6000.31c  7.7829E-04

26054.31c   3.30967E-03

26056.31c   5.19548E-02

26057.31c   1.19986E-03

26058.31c   1.59680E-04

24050.31c   6.99849E-04

24052.31c   1.34959E-02

24053.31c   1.53033E-03

24054.31c   3.80931E-04

28058.31c   6.12972E-03

28060.31c   2.36115E-03

28061.31c   1.02647E-04

28062.31c   3.27209E-04

28064.31c   8.33780E-05

42092.31c   2.17183E-05

42094.31c   1.35374E-05

42095.31c   2.32989E-05

42096.31c   2.44112E-05

42097.31c   1.39764E-05

42098.31c   3.53143E-05

42100.31c   1.40935E-05

25055.31c  1.1918E-03

13027.31c  3.4646E-04

29063.31c   5.10841E-05

29065.31c   2.27689E-05

22046.31c   2.41940E-05

22047.31c   2.18185E-05

22048.31c   2.16191E-04

22049.31c   1.58654E-05

22050.31c   1.51909E-05

14028.31c   9.22189E-04

14029.31c   4.66944E-05

14030.31c   3.09963E-05

23000.31c  9.2127E-05

1001.31c  2.2714E-05

kcode 10000 1. 50 350

ksrc 0 0 1.1

prdmp 3j 1

print

## D25. IEU-CT-02: IEU-COMP-THERM-002, case 3

MATR 17% - Gd

c                                                                         core

1  0                 -4  5 -3 (101:-121) (102:-121) (103:-121) (104:-121)

imp:n=1  fill=100

c                                     water between core and envelope cylinder

2  3 1.001640E-01  4 -6  5 -3  imp:n=1

c                                                            envelope cylinder

3  2 8.699752E-02  6 -7  2 -3  imp:n=1

c                                                                outside water

4  3 1.001640E-01  7 -1  2 -3  imp:n=1

c                                                       bottom water reflector

5  3 1.001640E-01    -8  2 -5  imp:n=1

c                                                             support cylinder

6  2 8.699752E-02  8 -9  2 -5  imp:n=1

c                         water between support cylinder and envelope cylinder

7  3 1.001640E-01  9 -6  2 -5  imp:n=1

c                                             empty tubes for the control rods

8  0               -111 122 -3  imp:n=1

9  2 8.699752E-02  -101 121 -3 (111:-122)  imp:n=1

10  0               -112 122 -3  imp:n=1

11  2 8.699752E-02  -102 121 -3 (112:-122)  imp:n=1

12  0               -113 122 -3  imp:n=1

13  2 8.699752E-02  -103 121 -3 (113:-122)  imp:n=1

14  0               -114 122 -3  imp:n=1

15  2 8.699752E-02  -104 121 -3 (114:-122)  imp:n=1

c

100  0  -201 202 -203 204  imp:n=1  lat=1  u=100

c  100  0  -201 202 -203 204 -205 206  imp:n=1  lat=2  u=100

fill=-7:7 -7:7 0:0

4 36r

2 2 1 1 2 2              4  7r

2 1 1 1 1 1 2             4  6r

1 1 1 1 1 1 1 1            4  5r

1 1 1 1 1 1 1 1 1           4  4r

2 1 1 1 1 1 1 1 1 1          4  3r

2 1 1 1 1 3 1 1 1 1 2         4  3r

1 1 1 1 1 1 1 1 1 2          4  4r

1 1 1 1 1 1 1 1 1           4  5r

1 1 1 1 1 1 1 1            4  6r

2 1 1 1 1 1 2             4  7r

2 2 1 1 2 2              4 36r

c

c                                                        universe 1 - fuel rod

c

c

c                                                                    1-st tube

1020  2 8.699752E-02  301 -302  402 -407  imp:n=1  u=-1

c                                                    1-st annular fuel element

11030  3 1.001640E-01  302 -304  402 -403  imp:n=1  u=-1

21030  2 8.699752E-02  302 -304  403 -404  imp:n=1  u=-1

1030  1 3.335478E-02  302 -303  404 -405  imp:n=1  u=-1

31030  2 8.699752E-02  302 -304  405 -406  imp:n=1  u=-1

41030  3 1.001640E-01  302 -304  406 -407  imp:n=1  u=-1

c                                                                    2-nd tube

1040  2 8.699752E-02  303 -304  404 -405  imp:n=1  u=-1

c                                                                    water gap

1050  3 1.001640E-01  304 -305  402 -407  imp:n=1  u=-1

c                                                                    3-rd tube

1060  2 8.699752E-02  305 -306  402 -407  imp:n=1  u=-1

c                                                    2-nd annular fuel element

11070  3 1.001640E-01  306 -308  402 -403  imp:n=1  u=-1

21070  2 8.699752E-02  306 -308  403 -404  imp:n=1  u=-1

1070  1 3.335478E-02  306 -307  404 -405  imp:n=1  u=-1

31070  2 8.699752E-02  306 -308  405 -406  imp:n=1  u=-1

41070  3 1.001640E-01  306 -308  406 -407  imp:n=1  u=-1

c                                                                    4-th tube

1080  2 8.699752E-02  307 -308  404 -405  imp:n=1  u=-1

c                                                                    water gap

1090  3 1.001640E-01  308 -309  402 -407  imp:n=1  u=-1

c                                                                    5-th tube

1100  2 8.699752E-02  309 -310  402 -407  imp:n=1  u=-1

c                                                                  bottom plug

1110  2 8.699752E-02      -310  401 -402  imp:n=1  u=-1

c                                                                     top plug

1120  2 8.699752E-02  301 -310  407 -408  imp:n=1  u=-1

c                                                    water outside of fuel rod

1130  3 1.001640E-01  310       401 -603  imp:n=1  u=1

c                                                         water above fuel rod

1140  3 1.001640E-01            419       imp:n=1  u=1

c                                     water between fuel rod and support plate

1150  3 1.001640E-01  300       602 -401  imp:n=1  u=1

c                                                          lower lattice plate

1160  3 1.001640E-01      -502      -601  imp:n=1  u=1

1170  2 8.699752E-02  502           -601  imp:n=1  u=1

c                                                                support plate

1180  3 1.001640E-01      -501  601 -602  #1500  imp:n=1  u=-1

1190  2 8.699752E-02  501       601 -602  imp:n=1  u=1

c                                                          upper lattice plate

1200  3 1.001640E-01  310 -502  603 -604  imp:n=1  u=-1

1210  2 8.699752E-02  502       603 -604  imp:n=1  u=1

c                                             water around top end of fuel rod

1220  3 1.001640E-01  310       604 -408  imp:n=1  u=1

c                                                                 absorber rod

1230  5 6.026200E-02      -311  402 -409  imp:n=1  u=-1

1240  3 1.001640E-01  311 -301  402 -409  imp:n=1  u=-1

c

1250  5 6.026200E-02      -314  409 -410  imp:n=1  u=-1

1260  3 1.001640E-01  314 -301  409 -410  imp:n=1  u=-1

c

1270  5 6.026200E-02      -313  410 -411  imp:n=1  u=-1

1280  3 1.001640E-01  313 -301  410 -411  imp:n=1  u=-1

c

1290  2 8.699752E-02      -311  411 -412  imp:n=1  u=-1

1300  5 6.026200E-02  311 -313  411 -412  imp:n=1  u=-1

1310  3 1.001640E-01  313 -301  411 -412  imp:n=1  u=-1

c

1320  2 8.699752E-02      -313  412 -413  imp:n=1  u=-1

1330  3 1.001640E-01  313 -301  412 -413  imp:n=1  u=-1

c

1340  4 4.233530E-02      -312  413 -414  imp:n=1  u=-1

1350  2 8.699752E-02  312 -313  413 -414  imp:n=1  u=-1

1360  3 1.001640E-01  313 -301  413 -414  imp:n=1  u=-1

c

1370  2 8.699752E-02      -313  414 -415  imp:n=1  u=-1

1380  3 1.001640E-01  313 -301  414 -415  imp:n=1  u=-1

c

1390  2 8.699752E-02      -311  415 -416  imp:n=1  u=-1

1400  5 6.026200E-02  311 -313  415 -416  imp:n=1  u=-1

1410  3 1.001640E-01  313 -301  415 -416  imp:n=1  u=-1

c

1420  5 6.026200E-02      -313  416 -417  imp:n=1  u=-1

1430  3 1.001640E-01  313 -301  416 -417  imp:n=1  u=-1

c

1440  5 6.026200E-02      -314  417 -418  imp:n=1  u=-1

1450  3 1.001640E-01  314 -301  417 -418  imp:n=1  u=-1

c

1460  5 6.026200E-02      -311  418 -419  imp:n=1  u=-1

1470  3 1.001640E-01  311 -301  418 -408  imp:n=1  u=-1

1490  3 1.001640E-01  311       408 -419  imp:n=1  u=1

c                                                                         cone

1500  2 8.699752E-02      -300  400 -401  imp:n=1  u=-1

c

c                               universe 2 - steel plates with holes and water

c                                                          lower lattice plate

201  3 1.001640E-01      -502      -601  imp:n=1  u=2

202  2 8.699752E-02  502           -601  imp:n=1  u=2

c                                                                support plate

203  3 1.001640E-01      -501  601 -602  imp:n=1  u=-2

204  2 8.699752E-02  501       601 -602  imp:n=1  u=2

c                                                                        water

205  3 1.001640E-01            602 -603  imp:n=1  u=2

c                                                          upper lattice plate

206  3 1.001640E-01      -502  603 -604  imp:n=1  u=-2

207  2 8.699752E-02  502       603 -604  imp:n=1  u=2

c                                                                        water

208  3 1.001640E-01            604       imp:n=1  u=2

c

c                                    universe 3 - central water-cooled channel

c                                                          lower lattice plate

301  3 1.001640E-01      -511      -601  imp:n=1  u=3

302  2 8.699752E-02  511           -601  imp:n=1  u=3

c                                                                support plate

303  3 1.001640E-01      -501  601 -602  imp:n=1  u=-3

304  2 8.699752E-02  501       601 -602  imp:n=1  u=3

c                         water between support plate and water-cooled channel

305  3 1.001640E-01            602 -401  imp:n=1  u=3

c                                                                central space

306  0                   -503  401       imp:n=1  u=3

c                                                                    1-st tube

307  2 8.699752E-02  503 -504  401       imp:n=1  u=3

c                                                                        water

308  3 1.001640E-01  504 -505  401       imp:n=1  u=3

c                                                                    2-nd tube

309  2 8.699752E-02  505 -506  401       imp:n=1  u=3

c                                                                        water

310  3 1.001640E-01  506 -507  401       imp:n=1  u=3

c                                                                    3-rd tube

311  2 8.699752E-02  507 -508  401       imp:n=1  u=3

c                                                                     void gap

312  0               508 -509  401       imp:n=1  u=3

c                                                                    4-th tube

313  2 8.699752E-02  509 -510  401       imp:n=1  u=3

c                                                                        water

314  3 1.001640E-01  510       401 -603  imp:n=1  u=3

c                                                          upper lattice plate

315  3 1.001640E-01  510 -511  603 -604  imp:n=1  u=-3

316  2 8.699752E-02  511       603 -604  imp:n=1  u=3

c                                                                        water

317  3 1.001640E-01  510       604       imp:n=1  u=3

c

c                                          universe 4 - steel plates and water

401  2 8.699752E-02                -602  imp:n=1  u=4

402  3 1.001640E-01            602 -603  imp:n=1  u=4

403  2 8.699752E-02            603 -604  imp:n=1  u=4

404  3 1.001640E-01            604       imp:n=1  u=4

c                                                                    supercell

9999  0 1:-2:3 imp:n=0

1  cz  60        $ water reflector outer radius

2  pz -19        $ water reflector (envelope cylinder) lower level

3  pz 106        $ water reflector (envelope cylinder) upper level

4  cz  41        $ support/lattice plates radius

5  pz   0        $ bottom support plate lower level

6  cz  42        $ envelope cylinder inner radius

7  cz  44        $ envelope cylinder outer radius

8  cz  40        $ support cylinder inner radius

9  cz  40.5      $ support cylinder outer radius

c

101  c/z  -13.74093640671   3.4  1.5

102  c/z   13.74093640671  -3.4  1.5

103  c/z  -3.925981830489  13.6  1.5

104  c/z   3.925981830489 -13.6  1.5

c

111  c/z  -13.74093640671   3.4  1.2

112  c/z   13.74093640671  -3.4  1.2

113  c/z  -3.925981830489  13.6  1.2

114  c/z   3.925981830489 -13.6  1.2

c

121  pz   4.000000000001

122  pz   4.3

c

201  px  2.944486372867

202  px -2.944486372867

203  p  -1  1.732050807569  0   5.888972745734

204  p  -1  1.732050807569  0  -5.888972745734

c

c  201  p   1.732050807569  1  0   6.8

c  202  p   1.732050807569  1  0  -6.8

c  203  py  3.4

c  204  py -3.4

c  205  p  -1.732050807569  1  0   6.8

c  206  p  -1.732050807569  1  0  -6.8

c

300  kz  2 0.25 1  $ cone

301  cz  1.17      $ 1-st tube inner radius

302  cz  1.2       $ 1-st tube outer radius

303  cz  1.43      $ 2-nd tube inner radius

304  cz  1.4640    $ 2-nd tube outer radius

305  cz  1.7968    $ 3-rd tube inner radius

306  cz  1.83      $ 3-rd tube outer radius

307  cz  2.06      $ 4-th tube inner radius

308  cz  2.09      $ 4-th tube outer radius

309  cz  2.26      $ 5-th tube inner radius

310  cz  2.29      $ 5-th tube outer radius

c

311  cz  0.3       $ tail outer radius

312  cz  0.52      $ absorber element tube inner radius

313  cz  0.55      $ absorber element tube outer radius

314  cz  1.15      $ flange outer radius

c

400  pz  3         $ lower cone plane

401  pz  4         $ lower surface of fuel rod bottom plug

402  pz  4.3       $ upper surface of fuel rod bottom plug

403  pz  5.7       $ lower surface of fuel bottom plug

404  pz  5.9       $ upper surface of fuel bottom plug

405  pz 65.9       $ lower surface of fuel top plug

406  pz 66.2       $ upper surface of fuel top plug

407  pz 68.6       $ lower surface of fuel rod top plug

408  pz 68.9       $ upper surface of fuel rod top plug

c

409  pz  6.3

410  pz  6.8

411  pz  9.9

412  pz 10.9

413  pz 11.9       $ lower surface of absorber element

414  pz 59.9       $ upper surface of absorber element

415  pz 60.9

416  pz 61.9

417  pz 67.4

418  pz 67.9

419  pz 70.4

c

501  cz  0.75      $ radius of hole in support plate

502  cz  2.35      $ radius of hole in lattice plate

503  cz  1.05      $ inner radius of 1-st tube in central channel

504  cz  1.1       $ outer radius of 1-st tube in central channel

505  cz  1.3       $ inner radius of 2-nd tube in central channel

506  cz  1.5       $ outer radius of 2-nd tube in central channel

507  cz  1.7       $ inner radius of 3-rd tube in central channel

508  cz  1.9       $ outer radius of 3-rd tube in central channel

509  cz  2.2       $ inner radius of 4-th tube in central channel

510  cz  2.5       $ outer radius of 4-th tube in central channel

511  cz  2.53      $ radius of hole for central channel

c

601  pz  1.5       $ upper surface of bottom lattice plate

602  pz  3.5       $ upper surface of support plate

603  pz 66.8       $ lower surface of top lattice plate

604  pz 68.8       $ upper surface of top lattice plate

m1      92234.31c  1.6683E-05

92235.31c  1.8827E-03

92238.31c  9.0594E-03

8016.31c  2.2396E-02

m2    26054.31c   3.50618E-03

26056.31c   5.50396E-02

26057.31c   1.27110E-03

26058.31c   1.69161E-04

24050.31c   6.83208E-04

24052.31c   1.31750E-02

24053.31c   1.49394E-03

24054.31c   3.71873E-04

28058.31c   5.78859E-03

28060.31c   2.22974E-03

28061.31c   9.69342E-05

28062.31c   3.08999E-04

28064.31c   7.87378E-05

25055.31c  1.0431E-03

14028.31c   7.84121E-04

14029.31c   3.97034E-05

14030.31c   2.63556E-05

22046.31c   3.90852E-05

22047.31c   3.52477E-05

22048.31c   3.49256E-04

22049.31c   2.56304E-05

22050.31c   2.45408E-05

6000.31c  4.1748E-04

m3       1001.31c  6.6776E-02

8016.31c  3.3388E-02

mt3 lwtr01.31t

m4      64152.31c  4.3186E-06

64154.31c  4.7073E-05

64155.31c  3.1958E-04

64156.31c  4.4201E-04

64157.31c  3.3793E-04

64158.31c  5.3637E-04

64160.31c  4.7202E-04

13027.31c  1.4775E-02

8016.31c  2.5401E-02

m5      13027.31c  6.0262E-02

kcode  5000 1.0 200 1200

sdef  pos=0 0 35.9 axs=0 0 1 rad=d1 ext=d2

si1  0 10

si2  10

prdmp  3j 1

print

## D26. STACY-36: LEU-SOL-THERM-007, case 36

file name=run032 ; STACY ( model 2 )

c    R036(bare)   ;U=253.9(g/lit) A=2.23(mol/lit) D=1.4102(g/cc)

c    Critical level  83.55(cm)

c

c    cellcard

c

1    1  9.89471078E-02          1  -2 -10        imp:n=1 u=1

2    3  4.94250000E-05          2  -3 -10        imp:n=1 u=1

3    2  8.68449842E-02   #1 #2                   imp:n=1 u=1

4    0                         -4   5 -20        imp:n=1 fill=1

5    0              #1 #2 #4                     imp:n=0

c    surface cards (origin x=0.0 y=0.0 z=0.0)

c    cylinder

1   pz      0.0

2   pz     83.55

3   pz    150.0

4   pz    152.5

5   pz     -2.0

10   cz     29.5

20   cz     29.8

c

c    data cards

c

mode  n                    $ transport neutrons only

c

c    material cards

c    atomic density =  9.89471078E-02

m1       1001.31c  5.8115E-02

7014.31c  2.6292E-03

8016.31c  3.7560E-02

92234.31c  5.2265E-07

92235.31c  6.4857E-05

92236.31c  6.4776E-08

92238.31c  5.7769E-04

mt1 lwtr01.31t    $  300K

c

c    sus304 7.93g/cm3 ; atomic density  8.68449842E-02

m2       6000.31c  4.3736E-05

14028.31c   9.80128E-04

14029.31c   4.96281E-05

14030.31c   3.29437E-05

25055.31c  1.1561E-03

15031.31c  4.3170E-05

16032.31c   2.82721E-06

16033.31c   2.26343E-08

16034.31c   1.27765E-07

16036.31c   5.95640E-10

28058.31c   5.67783E-03

28060.31c   2.18708E-03

28061.31c   9.50794E-05

28062.31c   3.03086E-04

28064.31c   7.72312E-05

24050.31c   7.28874E-04

24052.31c   1.40556E-02

24053.31c   1.59379E-03

24054.31c   3.96729E-04

26054.31c   3.47316E-03

26056.31c   5.45211E-02

26057.31c   1.25913E-03

26058.31c   1.67567E-04

c

c     Air (0.001184 g/cm3)

c     atomic density  4.9425E-05

m3       7014.31c  3.9016E-05

8016.31c  1.0409E-05

c

c    criticality cards

c

kcode   5000 1.0 50 2000

sdef  cel=d1 pos=0 0 0 axs=0 0 1 rad=d2 ext=d3 erg=d4

c

si1  l 4:1

sp1        1

c

si2    h   0.0   29.50

sp2   -21  1

c

si3    h   0.0   83.55

sp3   -21  0

c

sp4    -3

c

prdmp  j -100 1 3

c

print -175

## D27. B&W XI-2: LEU-COMP-THERM-008, case 2

B&W Criticals  Core XI Load 2  1335.5 PPM  Axially Uniform Octant  ENDF/B-VI

c    Central Assembly

1     3   0.10018       1   -2     3     4   -88                $ Water Hole

2     3   0.10018       1   -2     3     4    88   -89          $ Water Hole

3     3   0.10018       1   -2     3     4    89   -47          $ Water Hole

4     1   0.068525      1   -2     3   -90                      $ Fuel

5     2   0.055323      1   -2     3    90   -91                $ Clad

6     3   0.10018       1   -2     3    -6    47   -48    91    $ Water

7     1   0.068525      1   -2     3   -92                      $ Fuel

8     2   0.055323      1   -2     3    92   -93                $ Clad

9     3   0.10018       1   -2     3    -6    48   -49    93    $ Water

10    1   0.068525      1   -2     3   -94                      $ Fuel

11    2   0.055323      1   -2     3    94   -95                $ Clad

12    3   0.10018       1   -2     3    -6    49   -50    95    $ Water

13    1   0.068525      1   -2     3   -96                      $ Fuel

14    2   0.055323      1   -2     3    96   -97                $ Clad

15    3   0.10018       1   -2     3    -6    50   -51    97    $ Water

16    1   0.068525      1   -2     3   -98                      $ Fuel

17    2   0.055323      1   -2     3    98   -99                $ Clad

18    3   0.10018       1   -2     3    -6    51   -52    99    $ Water

19    1   0.068525      1   -2     3  -100                      $ Fuel

20    2   0.055323      1   -2     3   100  -101                $ Clad

21    3   0.10018       1   -2     3    -6    52   -53   101    $ Water

22    1   0.068525      1   -2     3  -102                      $ Fuel

23    2   0.055323      1   -2     3   102  -103                $ Clad

24    3   0.10018       1   -2     3    -6    53   -54   103    $ Water

25    1   0.068525      1   -2     4  -104                      $ Fuel

26    2   0.055323      1   -2     4   104  -105                $ Clad

27    3   0.10018       1   -2     4     6    -7   -48   105    $ Water

28    1   0.068525      1   -2  -106                            $ Fuel

29    2   0.055323      1   -2   106  -107                      $ Clad

30    3   0.10018       1   -2     6    -7    48   -49   107    $ Water

31    1   0.068525      1   -2  -108                            $ Fuel

32    2   0.055323      1   -2   108  -109                      $ Clad

33    3   0.10018       1   -2     6    -7    49   -50   109    $ Water

34    1   0.068525      1   -2  -110                            $ Fuel

35    2   0.055323      1   -2   110  -111                      $ Clad

36    3   0.10018       1   -2     6    -7    50   -51   111    $ Water

37    1   0.068525      1   -2  -112                            $ Fuel

38    2   0.055323      1   -2   112  -113                      $ Clad

39    3   0.10018       1   -2     6    -7    51   -52   113    $ Water

40    1   0.068525      1   -2  -114                            $ Fuel

41    2   0.055323      1   -2   114  -115                      $ Clad

42    3   0.10018       1   -2     6    -7    52   -53   115    $ Water

43    1   0.068525      1   -2  -116                            $ Fuel

44    2   0.055323      1   -2   116  -117                      $ Clad

45    3   0.10018       1   -2     6    -7    53   -54   117    $ Water

46    3   0.10018       1   -2     4  -118                      $ Water Hole

47    3   0.10018       1   -2     4   118  -119                $ Water Hole

48    3   0.10018       1   -2     4     7    -8   -49   119    $ Water Hole

49    1   0.068525      1   -2  -120                            $ Fuel

50    2   0.055323      1   -2   120  -121                      $ Clad

51    3   0.10018       1   -2     7    -8    49   -50   121    $ Water

52    1   0.068525      1   -2  -122                            $ Fuel

53    2   0.055323      1   -2   122  -123                      $ Clad

54    3   0.10018       1   -2     7    -8    50   -51   123    $ Water

55    3   0.10018       1   -2  -124                            $ Water Hole

56    3   0.10018       1   -2   124  -125                      $ Water Hole

57    3   0.10018       1   -2     7    -8    51   -52   125    $ Water Hole

58    1   0.068525      1   -2  -126                            $ Fuel

59    2   0.055323      1   -2   126  -127                      $ Clad

60    3   0.10018       1   -2     7    -8    52   -53   127    $ Water

61    1   0.068525      1   -2  -128                            $ Fuel

62    2   0.055323      1   -2   128  -129                      $ Clad

63    3   0.10018       1   -2     7    -8    53   -54   129    $ Water

64    1   0.068525      1   -2     4  -130                      $ Fuel

65    2   0.055323      1   -2     4   130  -131                $ Clad

66    3   0.10018       1   -2     4     8    -9   -50   131    $ Water

67    1   0.068525      1   -2  -132                            $ Fuel

68    2   0.055323      1   -2   132  -133                      $ Clad

69    3   0.10018       1   -2     8    -9    50   -51   133    $ Water

70    1   0.068525      1   -2  -134                            $ Fuel

71    2   0.055323      1   -2   134  -135                      $ Clad

72    3   0.10018       1   -2     8    -9    51   -52   135    $ Water

73    1   0.068525      1   -2  -136                            $ Fuel

74    2   0.055323      1   -2   136  -137                      $ Clad

75    3   0.10018       1   -2     8    -9    52   -53   137    $ Water

76    1   0.068525      1   -2  -138                            $ Fuel

77    2   0.055323      1   -2   138  -139                      $ Clad

78    3   0.10018       1   -2     8    -9    53   -54   139    $ Water

79    3   0.10018       1   -2     4  -140                      $ Water Hole

80    3   0.10018       1   -2     4   140  -141                $ Water Hole

81    3   0.10018       1   -2     4     9   -10   -51   141    $ Water Hole

82    1   0.068525      1   -2  -142                            $ Fuel

83    2   0.055323      1   -2   142  -143                      $ Clad

84    3   0.10018       1   -2     9   -10    51   -52   143    $ Water

85    1   0.068525      1   -2  -144                            $ Fuel

86    2   0.055323      1   -2   144  -145                      $ Clad

87    3   0.10018       1   -2     9   -10    52   -53   145    $ Water

88    1   0.068525      1   -2  -146                            $ Fuel

89    2   0.055323      1   -2   146  -147                      $ Clad

90    3   0.10018       1   -2     9   -10    53   -54   147    $ Water

91    1   0.068525      1   -2     4  -148                      $ Fuel

92    2   0.055323      1   -2     4   148  -149                $ Clad

93    3   0.10018       1   -2     4    10   -11   -52   149    $ Water

94    1   0.068525      1   -2  -150                            $ Fuel

95    2   0.055323      1   -2   150  -151                      $ Clad

96    3   0.10018       1   -2    10   -11    52   -53   151    $ Water

97    1   0.068525      1   -2  -152                            $ Fuel

98    2   0.055323      1   -2   152  -153                      $ Clad

99    3   0.10018       1   -2    10   -11    53   -54   153    $ Water

100   1   0.068525      1   -2     4  -154                      $ Fuel

101   2   0.055323      1   -2     4   154  -155                $ Clad

102   3   0.10018       1   -2     4    11   -12   -53   155    $ Water

103   1   0.068525      1   -2  -156                            $ Fuel

104   2   0.055323      1   -2   156  -157                      $ Clad

105   3   0.10018       1   -2    11   -12    53   -54   157    $ Water

106   1   0.068525      1   -2     4  -158                      $ Fuel

107   2   0.055323      1   -2     4   158  -159                $ Clad

108   3   0.10018       1   -2     4    12   -13   -54   159    $ Water

c    Right Central Assembly

109   1   0.068525      1   -2     3  -160                      $ Fuel

110   2   0.055323      1   -2     3   160  -161                $ Clad

111   3   0.10018       1   -2     3    -6    54   -55   161    $ Water

112   1   0.068525      1   -2     3  -162                      $ Fuel

113   2   0.055323      1   -2     3   162  -163                $ Clad

114   3   0.10018       1   -2     3    -6    55   -56   163    $ Water

115   1   0.068525      1   -2     3  -164                      $ Fuel

116   2   0.055323      1   -2     3   164  -165                $ Clad

117   3   0.10018       1   -2     3    -6    56   -57   165    $ Water

118   1   0.068525      1   -2     3  -166                      $ Fuel

119   2   0.055323      1   -2     3   166  -167                $ Clad

120   3   0.10018       1   -2     3    -6    57   -58   167    $ Water

121   1   0.068525      1   -2     3  -168                      $ Fuel

122   2   0.055323      1   -2     3   168  -169                $ Clad

123   3   0.10018       1   -2     3    -6    58   -59   169    $ Water

124   1   0.068525      1   -2     3  -170                      $ Fuel

125   2   0.055323      1   -2     3   170  -171                $ Clad

126   3   0.10018       1   -2     3    -6    59   -60   171    $ Water

127   1   0.068525      1   -2     3  -172                      $ Fuel

128   2   0.055323      1   -2     3   172  -173                $ Clad

129   3   0.10018       1   -2     3    -6    60   -61   173    $ Water

130   3   0.10018       1   -2     3  -174                      $ Water Hole

131   3   0.10018       1   -2     3   174  -175                $ Water Hole

132   3   0.10018       1   -2     3    -6    61   -62   175    $ Water Hole

133   1   0.068525      1   -2     3  -176                      $ Fuel

134   2   0.055323      1   -2     3   176  -177                $ Clad

135   3   0.10018       1   -2     3    -6    62   -63   177    $ Water

136   1   0.068525      1   -2     3  -178                      $ Fuel

137   2   0.055323      1   -2     3   178  -179                $ Clad

138   3   0.10018       1   -2     3    -6    63   -64   179    $ Water

139   1   0.068525      1   -2     3  -180                      $ Fuel

140   2   0.055323      1   -2     3   180  -181                $ Clad

141   3   0.10018       1   -2     3    -6    64   -65   181    $ Water

142   1   0.068525      1   -2     3  -182                      $ Fuel

143   2   0.055323      1   -2     3   182  -183                $ Clad

144   3   0.10018       1   -2     3    -6    65   -66   183    $ Water

145   1   0.068525      1   -2     3  -184                      $ Fuel

146   2   0.055323      1   -2     3   184  -185                $ Clad

147   3   0.10018       1   -2     3    -6    66   -67   185    $ Water

148   1   0.068525      1   -2     3  -186                      $ Fuel

149   2   0.055323      1   -2     3   186  -187                $ Clad

150   3   0.10018       1   -2     3    -6    67   -68   187    $ Water

151   1   0.068525      1   -2     3  -188                      $ Fuel

152   2   0.055323      1   -2     3   188  -189                $ Clad

153   3   0.10018       1   -2     3    -6    68   -69   189    $ Water

154   1   0.068525      1   -2  -190                            $ Fuel

155   2   0.055323      1   -2   190  -191                      $ Clad

156   3   0.10018       1   -2     6    -7    54   -55   191    $ Water

157   1   0.068525      1   -2  -192                            $ Fuel

158   2   0.055323      1   -2   192  -193                      $ Clad

159   3   0.10018       1   -2     6    -7    55   -56   193    $ Water

160   1   0.068525      1   -2  -194                            $ Fuel

161   2   0.055323      1   -2   194  -195                      $ Clad

162   3   0.10018       1   -2     6    -7    56   -57   195    $ Water

163   1   0.068525      1   -2  -196                            $ Fuel

164   2   0.055323      1   -2   196  -197                      $ Clad

165   3   0.10018       1   -2     6    -7    57   -58   197    $ Water

166   1   0.068525      1   -2  -198                            $ Fuel

167   2   0.055323      1   -2   198  -199                      $ Clad

168   3   0.10018       1   -2     6    -7    58   -59   199    $ Water

169   1   0.068525      1   -2  -200                            $ Fuel

170   2   0.055323      1   -2   200  -201                      $ Clad

171   3   0.10018       1   -2     6    -7    59   -60   201    $ Water

172   1   0.068525      1   -2  -202                            $ Fuel

173   2   0.055323      1   -2   202  -203                      $ Clad

174   3   0.10018       1   -2     6    -7    60   -61   203    $ Water

175   1   0.068525      1   -2  -204                            $ Fuel

176   2   0.055323      1   -2   204  -205                      $ Clad

177   3   0.10018       1   -2     6    -7    61   -62   205    $ Water

178   1   0.068525      1   -2  -206                            $ Fuel

179   2   0.055323      1   -2   206  -207                      $ Clad

180   3   0.10018       1   -2     6    -7    62   -63   207    $ Water

181   1   0.068525      1   -2  -208                            $ Fuel

182   2   0.055323      1   -2   208  -209                      $ Clad

183   3   0.10018       1   -2     6    -7    63   -64   209    $ Water

184   1   0.068525      1   -2  -210                            $ Fuel

185   2   0.055323      1   -2   210  -211                      $ Clad

186   3   0.10018       1   -2     6    -7    64   -65   211    $ Water

187   1   0.068525      1   -2  -212                            $ Fuel

188   2   0.055323      1   -2   212  -213                      $ Clad

189   3   0.10018       1   -2     6    -7    65   -66   213    $ Water

190   1   0.068525      1   -2  -214                            $ Fuel

191   2   0.055323      1   -2   214  -215                      $ Clad

192   3   0.10018       1   -2     6    -7    66   -67   215    $ Water

193   1   0.068525      1   -2  -216                            $ Fuel

194   2   0.055323      1   -2   216  -217                      $ Clad

195   3   0.10018       1   -2     6    -7    67   -68   217    $ Water

196   1   0.068525      1   -2  -218                            $ Fuel

197   2   0.055323      1   -2   218  -219                      $ Clad

198   3   0.10018       1   -2     6    -7    68   -69   219    $ Water

199   1   0.068525      1   -2  -220                            $ Fuel

200   2   0.055323      1   -2   220  -221                      $ Clad

201   3   0.10018       1   -2     7    -8    54   -55   221    $ Water

202   1   0.068525      1   -2  -222                            $ Fuel

203   2   0.055323      1   -2   222  -223                      $ Clad

204   3   0.10018       1   -2     7    -8    55   -56   223    $ Water

205   3   0.10018       1   -2  -224                            $ Water Hole

206   3   0.10018       1   -2   224  -225                      $ Water Hole

207   3   0.10018       1   -2     7    -8    56   -57   225    $ Water Hole

208   1   0.068525      1   -2  -226                            $ Fuel

209   2   0.055323      1   -2   226  -227                      $ Clad

210   3   0.10018       1   -2     7    -8    57   -58   227    $ Water

211   1   0.068525      1   -2  -228                            $ Fuel

212   2   0.055323      1   -2   228  -229                      $ Clad

213   3   0.10018       1   -2     7    -8    58   -59   229    $ Water

214   3   0.10018       1   -2  -230                            $ Water Hole

215   3   0.10018       1   -2   230  -231                      $ Water Hole

216   3   0.10018       1   -2     7    -8    59   -60   231    $ Water Hole

217   1   0.068525      1   -2  -232                            $ Fuel

218   2   0.055323      1   -2   232  -233                      $ Clad

219   3   0.10018       1   -2     7    -8    60   -61   233    $ Water

220   1   0.068525      1   -2  -234                            $ Fuel

221   2   0.055323      1   -2   234  -235                      $ Clad

222   3   0.10018       1   -2     7    -8    61   -62   235    $ Water

223   1   0.068525      1   -2  -236                            $ Fuel

224   2   0.055323      1   -2   236  -237                      $ Clad

225   3   0.10018       1   -2     7    -8    62   -63   237    $ Water

226   3   0.10018       1   -2  -238                            $ Water Hole

227   3   0.10018       1   -2   238  -239                      $ Water Hole

228   3   0.10018       1   -2     7    -8    63   -64   239    $ Water Hole

229   1   0.068525      1   -2  -240                            $ Fuel

230   2   0.055323      1   -2   240  -241                      $ Clad

231   3   0.10018       1   -2     7    -8    64   -65   241    $ Water

232   1   0.068525      1   -2  -242                            $ Fuel

233   2   0.055323      1   -2   242  -243                      $ Clad

234   3   0.10018       1   -2     7    -8    65   -66   243    $ Water

235   3   0.10018       1   -2  -244                            $ Water Hole

236   3   0.10018       1   -2   244  -245                      $ Water Hole

237   3   0.10018       1   -2     7    -8    66   -67   245    $ Water Hole

238   1   0.068525      1   -2  -246                            $ Fuel

239   2   0.055323      1   -2   246  -247                      $ Clad

240   3   0.10018       1   -2     7    -8    67   -68   247    $ Water

241   1   0.068525      1   -2  -248                            $ Fuel

242   2   0.055323      1   -2   248  -249                      $ Clad

243   3   0.10018       1   -2     7    -8    68   -69   249    $ Water

244   1   0.068525      1   -2  -250                            $ Fuel

245   2   0.055323      1   -2   250  -251                      $ Clad

246   3   0.10018       1   -2     8    -9    54   -55   251    $ Water

247   1   0.068525      1   -2  -252                            $ Fuel

248   2   0.055323      1   -2   252  -253                      $ Clad

249   3   0.10018       1   -2     8    -9    55   -56   253    $ Water

250   1   0.068525      1   -2  -254                            $ Fuel

251   2   0.055323      1   -2   254  -255                      $ Clad

252   3   0.10018       1   -2     8    -9    56   -57   255    $ Water

253   1   0.068525      1   -2  -256                            $ Fuel

254   2   0.055323      1   -2   256  -257                      $ Clad

255   3   0.10018       1   -2     8    -9    57   -58   257    $ Water

256   1   0.068525      1   -2  -258                            $ Fuel

257   2   0.055323      1   -2   258  -259                      $ Clad

258   3   0.10018       1   -2     8    -9    58   -59   259    $ Water

259   1   0.068525      1   -2  -260                            $ Fuel

260   2   0.055323      1   -2   260  -261                      $ Clad

261   3   0.10018       1   -2     8    -9    59   -60   261    $ Water

262   1   0.068525      1   -2  -262                            $ Fuel

263   2   0.055323      1   -2   262  -263                      $ Clad

264   3   0.10018       1   -2     8    -9    60   -61   263    $ Water

265   1   0.068525      1   -2  -264                            $ Fuel

266   2   0.055323      1   -2   264  -265                      $ Clad

267   3   0.10018       1   -2     8    -9    61   -62   265    $ Water

268   1   0.068525      1   -2  -266                            $ Fuel

269   2   0.055323      1   -2   266  -267                      $ Clad

270   3   0.10018       1   -2     8    -9    62   -63   267    $ Water

271   1   0.068525      1   -2  -268                            $ Fuel

272   2   0.055323      1   -2   268  -269                      $ Clad

273   3   0.10018       1   -2     8    -9    63   -64   269    $ Water

274   1   0.068525      1   -2  -270                            $ Fuel

275   2   0.055323      1   -2   270  -271                      $ Clad

276   3   0.10018       1   -2     8    -9    64   -65   271    $ Water

277   1   0.068525      1   -2  -272                            $ Fuel

278   2   0.055323      1   -2   272  -273                      $ Clad

279   3   0.10018       1   -2     8    -9    65   -66   273    $ Water

280   1   0.068525      1   -2  -274                            $ Fuel

281   2   0.055323      1   -2   274  -275                      $ Clad

282   3   0.10018       1   -2     8    -9    66   -67   275    $ Water

283   1   0.068525      1   -2  -276                            $ Fuel

284   2   0.055323      1   -2   276  -277                      $ Clad

285   3   0.10018       1   -2     8    -9    67   -68   277    $ Water

286   1   0.068525      1   -2  -278                            $ Fuel

287   2   0.055323      1   -2   278  -279                      $ Clad

288   3   0.10018       1   -2     8    -9    68   -69   279    $ Water

289   1   0.068525      1   -2  -280                            $ Fuel

290   2   0.055323      1   -2   280  -281                      $ Clad

291   3   0.10018       1   -2     9   -10    54   -55   281    $ Water

292   1   0.068525      1   -2  -282                            $ Fuel

293   2   0.055323      1   -2   282  -283                      $ Clad

294   3   0.10018       1   -2     9   -10    55   -56   283    $ Water

295   1   0.068525      1   -2  -284                            $ Fuel

296   2   0.055323      1   -2   284  -285                      $ Clad

297   3   0.10018       1   -2     9   -10    56   -57   285    $ Water

298   3   0.10018       1   -2  -286                            $ Water Hole

299   3   0.10018       1   -2   286  -287                      $ Water Hole

300   3   0.10018       1   -2     9   -10    57   -58   287    $ Water Hole

301   1   0.068525      1   -2  -288                            $ Fuel

302   2   0.055323      1   -2   288  -289                      $ Clad

303   3   0.10018       1   -2     9   -10    58   -59   289    $ Water

304   1   0.068525      1   -2  -290                            $ Fuel

305   2   0.055323      1   -2   290  -291                      $ Clad

306   3   0.10018       1   -2     9   -10    59   -60   291    $ Water

307   1   0.068525      1   -2  -292                            $ Fuel

308   2   0.055323      1   -2   292  -293                      $ Clad

309   3   0.10018       1   -2     9   -10    60   -61   293    $ Water

310   1   0.068525      1   -2  -294                            $ Fuel

311   2   0.055323      1   -2   294  -295                      $ Clad

312   3   0.10018       1   -2     9   -10    61   -62   295    $ Water

313   1   0.068525      1   -2  -296                            $ Fuel

314   2   0.055323      1   -2   296  -297                      $ Clad

315   3   0.10018       1   -2     9   -10    62   -63   297    $ Water

316   1   0.068525      1   -2  -298                            $ Fuel

317   2   0.055323      1   -2   298  -299                      $ Clad

318   3   0.10018       1   -2     9   -10    63   -64   299    $ Water

319   1   0.068525      1   -2  -300                            $ Fuel

320   2   0.055323      1   -2   300  -301                      $ Clad

321   3   0.10018       1   -2     9   -10    64   -65   301    $ Water

322   3   0.10018       1   -2  -302                            $ Water Hole

323   3   0.10018       1   -2   302  -303                      $ Water Hole

324   3   0.10018       1   -2     9   -10    65   -66   303    $ Water Hole

325   1   0.068525      1   -2  -304                            $ Fuel

326   2   0.055323      1   -2   304  -305                      $ Clad

327   3   0.10018       1   -2     9   -10    66   -67   305    $ Water

328   1   0.068525      1   -2  -306                            $ Fuel

329   2   0.055323      1   -2   306  -307                      $ Clad

330   3   0.10018       1   -2     9   -10    67   -68   307    $ Water

331   1   0.068525      1   -2  -308                            $ Fuel

332   2   0.055323      1   -2   308  -309                      $ Clad

333   3   0.10018       1   -2     9   -10    68   -69   309    $ Water

334   1   0.068525      1   -2  -310                            $ Fuel

335   2   0.055323      1   -2   310  -311                      $ Clad

336   3   0.10018       1   -2    10   -11    54   -55   311    $ Water

337   1   0.068525      1   -2  -312                            $ Fuel

338   2   0.055323      1   -2   312  -313                      $ Clad

339   3   0.10018       1   -2    10   -11    55   -56   313    $ Water

340   1   0.068525      1   -2  -314                            $ Fuel

341   2   0.055323      1   -2   314  -315                      $ Clad

342   3   0.10018       1   -2    10   -11    56   -57   315    $ Water

343   1   0.068525      1   -2  -316                            $ Fuel

344   2   0.055323      1   -2   316  -317                      $ Clad

345   3   0.10018       1   -2    10   -11    57   -58   317    $ Water

346   1   0.068525      1   -2  -318                            $ Fuel

347   2   0.055323      1   -2   318  -319                      $ Clad

348   3   0.10018       1   -2    10   -11    58   -59   319    $ Water

349   3   0.10018       1   -2  -320                            $ Water Hole

350   3   0.10018       1   -2   320  -321                      $ Water Hole

351   3   0.10018       1   -2    10   -11    59   -60   321    $ Water Hole

352   1   0.068525      1   -2  -322                            $ Fuel

353   2   0.055323      1   -2   322  -323                      $ Clad

354   3   0.10018       1   -2    10   -11    60   -61   323    $ Water

355   1   0.068525      1   -2  -324                            $ Fuel

356   2   0.055323      1   -2   324  -325                      $ Clad

357   3   0.10018       1   -2    10   -11    61   -62   325    $ Water

358   1   0.068525      1   -2  -326                            $ Fuel

359   2   0.055323      1   -2   326  -327                      $ Clad

360   3   0.10018       1   -2    10   -11    62   -63   327    $ Water

361   3   0.10018       1   -2  -328                            $ Water Hole

362   3   0.10018       1   -2   328  -329                      $ Water Hole

363   3   0.10018       1   -2    10   -11    63   -64   329    $ Water Hole

364   1   0.068525      1   -2  -330                            $ Fuel

365   2   0.055323      1   -2   330  -331                      $ Clad

366   3   0.10018       1   -2    10   -11    64   -65   331    $ Water

367   1   0.068525      1   -2  -332                            $ Fuel

368   2   0.055323      1   -2   332  -333                      $ Clad

369   3   0.10018       1   -2    10   -11    65   -66   333    $ Water

370   1   0.068525      1   -2  -334                            $ Fuel

371   2   0.055323      1   -2   334  -335                      $ Clad

372   3   0.10018       1   -2    10   -11    66   -67   335    $ Water

373   1   0.068525      1   -2  -336                            $ Fuel

374   2   0.055323      1   -2   336  -337                      $ Clad

375   3   0.10018       1   -2    10   -11    67   -68   337    $ Water

376   1   0.068525      1   -2  -338                            $ Fuel

377   2   0.055323      1   -2   338  -339                      $ Clad

378   3   0.10018       1   -2    10   -11    68   -69   339    $ Water

379   1   0.068525      1   -2  -340                            $ Fuel

380   2   0.055323      1   -2   340  -341                      $ Clad

381   3   0.10018       1   -2    11   -12    54   -55   341    $ Water

382   1   0.068525      1   -2  -342                            $ Fuel

383   2   0.055323      1   -2   342  -343                      $ Clad

384   3   0.10018       1   -2    11   -12    55   -56   343    $ Water

385   1   0.068525      1   -2  -344                            $ Fuel

386   2   0.055323      1   -2   344  -345                      $ Clad

387   3   0.10018       1   -2    11   -12    56   -57   345    $ Water

388   1   0.068525      1   -2  -346                            $ Fuel

389   2   0.055323      1   -2   346  -347                      $ Clad

390   3   0.10018       1   -2    11   -12    57   -58   347    $ Water

391   1   0.068525      1   -2  -348                            $ Fuel

392   2   0.055323      1   -2   348  -349                      $ Clad

393   3   0.10018       1   -2    11   -12    58   -59   349    $ Water

394   1   0.068525      1   -2  -350                            $ Fuel

395   2   0.055323      1   -2   350  -351                      $ Clad

396   3   0.10018       1   -2    11   -12    59   -60   351    $ Water

397   1   0.068525      1   -2  -352                            $ Fuel

398   2   0.055323      1   -2   352  -353                      $ Clad

399   3   0.10018       1   -2    11   -12    60   -61   353    $ Water

400   1   0.068525      1   -2  -354                            $ Fuel

401   2   0.055323      1   -2   354  -355                      $ Clad

402   3   0.10018       1   -2    11   -12    61   -62   355    $ Water

403   1   0.068525      1   -2  -356                            $ Fuel

404   2   0.055323      1   -2   356  -357                      $ Clad

405   3   0.10018       1   -2    11   -12    62   -63   357    $ Water

406   1   0.068525      1   -2  -358                            $ Fuel

407   2   0.055323      1   -2   358  -359                      $ Clad

408   3   0.10018       1   -2    11   -12    63   -64   359    $ Water

409   1   0.068525      1   -2  -360                            $ Fuel

410   2   0.055323      1   -2   360  -361                      $ Clad

411   3   0.10018       1   -2    11   -12    64   -65   361    $ Water

412   1   0.068525      1   -2  -362                            $ Fuel

413   2   0.055323      1   -2   362  -363                      $ Clad

414   3   0.10018       1   -2    11   -12    65   -66   363    $ Water

415   1   0.068525      1   -2  -364                            $ Fuel

416   2   0.055323      1   -2   364  -365                      $ Clad

417   3   0.10018       1   -2    11   -12    66   -67   365    $ Water

418   1   0.068525      1   -2  -366                            $ Fuel

419   2   0.055323      1   -2   366  -367                      $ Clad

420   3   0.10018       1   -2    11   -12    67   -68   367    $ Water

421   1   0.068525      1   -2  -368                            $ Fuel

422   2   0.055323      1   -2   368  -369                      $ Clad

423   3   0.10018       1   -2    11   -12    68   -69   369    $ Water

424   1   0.068525      1   -2  -370                            $ Fuel

425   2   0.055323      1   -2   370  -371                      $ Clad

426   3   0.10018       1   -2    12   -13    54   -55   371    $ Water

427   1   0.068525      1   -2  -372                            $ Fuel

428   2   0.055323      1   -2   372  -373                      $ Clad

429   3   0.10018       1   -2    12   -13    55   -56   373    $ Water

430   1   0.068525      1   -2  -374                            $ Fuel

431   2   0.055323      1   -2   374  -375                      $ Clad

432   3   0.10018       1   -2    12   -13    56   -57   375    $ Water

433   1   0.068525      1   -2  -376                            $ Fuel

434   2   0.055323      1   -2   376  -377                      $ Clad

435   3   0.10018       1   -2    12   -13    57   -58   377    $ Water

436   1   0.068525      1   -2  -378                            $ Fuel

437   2   0.055323      1   -2   378  -379                      $ Clad

438   3   0.10018       1   -2    12   -13    58   -59   379    $ Water

439   1   0.068525      1   -2  -380                            $ Fuel

440   2   0.055323      1   -2   380  -381                      $ Clad

441   3   0.10018       1   -2    12   -13    59   -60   381    $ Water

442   1   0.068525      1   -2  -382                            $ Fuel

443   2   0.055323      1   -2   382  -383                      $ Clad

444   3   0.10018       1   -2    12   -13    60   -61   383    $ Water

445   1   0.068525      1   -2  -384                            $ Fuel

446   2   0.055323      1   -2   384  -385                      $ Clad

447   3   0.10018       1   -2    12   -13    61   -62   385    $ Water

448   1   0.068525      1   -2  -386                            $ Fuel

449   2   0.055323      1   -2   386  -387                      $ Clad

450   3   0.10018       1   -2    12   -13    62   -63   387    $ Water

451   1   0.068525      1   -2  -388                            $ Fuel

452   2   0.055323      1   -2   388  -389                      $ Clad

453   3   0.10018       1   -2    12   -13    63   -64   389    $ Water

454   1   0.068525      1   -2  -390                            $ Fuel

455   2   0.055323      1   -2   390  -391                      $ Clad

456   3   0.10018       1   -2    12   -13    64   -65   391    $ Water

457   1   0.068525      1   -2  -392                            $ Fuel

458   2   0.055323      1   -2   392  -393                      $ Clad

459   3   0.10018       1   -2    12   -13    65   -66   393    $ Water

460   1   0.068525      1   -2  -394                            $ Fuel

461   2   0.055323      1   -2   394  -395                      $ Clad

462   3   0.10018       1   -2    12   -13    66   -67   395    $ Water

463   1   0.068525      1   -2  -396                            $ Fuel

464   2   0.055323      1   -2   396  -397                      $ Clad

465   3   0.10018       1   -2    12   -13    67   -68   397    $ Water

466   1   0.068525      1   -2  -398                            $ Fuel

467   2   0.055323      1   -2   398  -399                      $ Clad

468   3   0.10018       1   -2    12   -13    68   -69   399    $ Water

c    Upper Right Assembly

469   1   0.068525      1   -2     4  -400                      $ Fuel

470   2   0.055323      1   -2     4   400  -401                $ Clad

471   3   0.10018       1   -2     4    13    54   -55   401    $ Water

472   1   0.068525      1   -2  -402                            $ Fuel

473   2   0.055323      1   -2   402  -403                      $ Clad

474   3   0.10018       1   -2    13   -14    55   -56   403    $ Water

475   1   0.068525      1   -2  -404                            $ Fuel

476   2   0.055323      1   -2   404  -405                      $ Clad

477   3   0.10018       1   -2    13   -14    56   -57   405    $ Water

478   1   0.068525      1   -2  -406                            $ Fuel

479   2   0.055323      1   -2   406  -407                      $ Clad

480   3   0.10018       1   -2    13   -14    57   -58   407    $ Water

481   1   0.068525      1   -2  -408                            $ Fuel

482   2   0.055323      1   -2   408  -409                      $ Clad

483   3   0.10018       1   -2    13   -14    58   -59   409    $ Water

484   1   0.068525      1   -2  -410                            $ Fuel

485   2   0.055323      1   -2   410  -411                      $ Clad

486   3   0.10018       1   -2    13   -14    59   -60   411    $ Water

487   1   0.068525      1   -2  -412                            $ Fuel

488   2   0.055323      1   -2   412  -413                      $ Clad

489   3   0.10018       1   -2    13   -14    60   -61   413    $ Water

490   1   0.068525      1   -2  -414                            $ Fuel

491   2   0.055323      1   -2   414  -415                      $ Clad

492   3   0.10018       1   -2    13   -14    61   -62   415    $ Water

493   1   0.068525      1   -2  -416                            $ Fuel

494   2   0.055323      1   -2   416  -417                      $ Clad

495   3   0.10018       1   -2    13   -14    62   -63   417    $ Water

496   1   0.068525      1   -2  -418                            $ Fuel

497   2   0.055323      1   -2   418  -419                      $ Clad

498   3   0.10018       1   -2    13   -14    63   -64   419    $ Water

499   1   0.068525      1   -2  -420                            $ Fuel

500   2   0.055323      1   -2   420  -421                      $ Clad

501   3   0.10018       1   -2    13   -14    64   -65   421    $ Water

502   1   0.068525      1   -2  -422                            $ Fuel

503   2   0.055323      1   -2   422  -423                      $ Clad

504   3   0.10018       1   -2    13   -14    65   -66   423    $ Water

505   1   0.068525      1   -2  -424                            $ Fuel

506   2   0.055323      1   -2   424  -425                      $ Clad

507   3   0.10018       1   -2    13   -14    66   -67   425    $ Water

508   1   0.068525      1   -2  -426                            $ Fuel

509   2   0.055323      1   -2   426  -427                      $ Clad

510   3   0.10018       1   -2    13   -14    67   -68   427    $ Water

511   1   0.068525      1   -2  -428                            $ Fuel

512   2   0.055323      1   -2   428  -429                      $ Clad

513   3   0.10018       1   -2    13   -14    68   -69   429    $ Water

514   1   0.068525      1   -2     4  -430                      $ Fuel

515   2   0.055323      1   -2     4   430  -431                $ Clad

516   3   0.10018       1   -2     4    14    55   -56   431    $ Water

517   1   0.068525      1   -2  -432                            $ Fuel

518   2   0.055323      1   -2   432  -433                      $ Clad

519   3   0.10018       1   -2    14   -15    56   -57   433    $ Water

520   1   0.068525      1   -2  -434                            $ Fuel

521   2   0.055323      1   -2   434  -435                      $ Clad

522   3   0.10018       1   -2    14   -15    57   -58   435    $ Water

523   1   0.068525      1   -2  -436                            $ Fuel

524   2   0.055323      1   -2   436  -437                      $ Clad

525   3   0.10018       1   -2    14   -15    58   -59   437    $ Water

526   1   0.068525      1   -2  -438                            $ Fuel

527   2   0.055323      1   -2   438  -439                      $ Clad

528   3   0.10018       1   -2    14   -15    59   -60   439    $ Water

529   1   0.068525      1   -2  -440                            $ Fuel

530   2   0.055323      1   -2   440  -441                      $ Clad

531   3   0.10018       1   -2    14   -15    60   -61   441    $ Water

532   1   0.068525      1   -2  -442                            $ Fuel

533   2   0.055323      1   -2   442  -443                      $ Clad

534   3   0.10018       1   -2    14   -15    61   -62   443    $ Water

535   1   0.068525      1   -2  -444                            $ Fuel

536   2   0.055323      1   -2   444  -445                      $ Clad

537   3   0.10018       1   -2    14   -15    62   -63   445    $ Water

538   1   0.068525      1   -2  -446                            $ Fuel

539   2   0.055323      1   -2   446  -447                      $ Clad

540   3   0.10018       1   -2    14   -15    63   -64   447    $ Water

541   1   0.068525      1   -2  -448                            $ Fuel

542   2   0.055323      1   -2   448  -449                      $ Clad

543   3   0.10018       1   -2    14   -15    64   -65   449    $ Water

544   1   0.068525      1   -2  -450                            $ Fuel

545   2   0.055323      1   -2   450  -451                      $ Clad

546   3   0.10018       1   -2    14   -15    65   -66   451    $ Water

547   1   0.068525      1   -2  -452                            $ Fuel

548   2   0.055323      1   -2   452  -453                      $ Clad

549   3   0.10018       1   -2    14   -15    66   -67   453    $ Water

550   1   0.068525      1   -2  -454                            $ Fuel

551   2   0.055323      1   -2   454  -455                      $ Clad

552   3   0.10018       1   -2    14   -15    67   -68   455    $ Water

553   1   0.068525      1   -2  -456                            $ Fuel

554   2   0.055323      1   -2   456  -457                      $ Clad

555   3   0.10018       1   -2    14   -15    68   -69   457    $ Water

556   1   0.068525      1   -2     4  -458                      $ Fuel

557   2   0.055323      1   -2     4   458  -459                $ Clad

558   3   0.10018       1   -2     4    15    56   -57   459    $ Water

559   1   0.068525      1   -2  -460                            $ Fuel

560   2   0.055323      1   -2   460  -461                      $ Clad

561   3   0.10018       1   -2    15   -16    57   -58   461    $ Water

562   1   0.068525      1   -2  -462                            $ Fuel

563   2   0.055323      1   -2   462  -463                      $ Clad

564   3   0.10018       1   -2    15   -16    58   -59   463    $ Water

565   3   0.10018       1   -2  -464                            $ Water Hole

566   3   0.10018       1   -2   464  -465                      $ Water Hole

567   3   0.10018       1   -2    15   -16    59   -60   465    $ Water Hole

568   1   0.068525      1   -2  -466                            $ Fuel

569   2   0.055323      1   -2   466  -467                      $ Clad

570   3   0.10018       1   -2    15   -16    60   -61   467    $ Water

571   1   0.068525      1   -2  -468                            $ Fuel

572   2   0.055323      1   -2   468  -469                      $ Clad

573   3   0.10018       1   -2    15   -16    61   -62   469    $ Water

574   1   0.068525      1   -2  -470                            $ Fuel

575   2   0.055323      1   -2   470  -471                      $ Clad

576   3   0.10018       1   -2    15   -16    62   -63   471    $ Water

577   3   0.10018       1   -2  -472                            $ Water Hole

578   3   0.10018       1   -2   472  -473                      $ Water Hole

579   3   0.10018       1   -2    15   -16    63   -64   473    $ Water Hole

580   1   0.068525      1   -2  -474                            $ Fuel

581   2   0.055323      1   -2   474  -475                      $ Clad

582   3   0.10018       1   -2    15   -16    64   -65   475    $ Water

583   1   0.068525      1   -2  -476                            $ Fuel

584   2   0.055323      1   -2   476  -477                      $ Clad

585   3   0.10018       1   -2    15   -16    65   -66   477    $ Water

586   1   0.068525      1   -2  -478                            $ Fuel

587   2   0.055323      1   -2   478  -479                      $ Clad

588   3   0.10018       1   -2    15   -16    66   -67   479    $ Water

589   1   0.068525      1   -2  -480                            $ Fuel

590   2   0.055323      1   -2   480  -481                      $ Clad

591   3   0.10018       1   -2    15   -16    67   -68   481    $ Water

592   1   0.068525      1   -2  -482                            $ Fuel

593   2   0.055323      1   -2   482  -483                      $ Clad

594   3   0.10018       1   -2    15   -16    68   -69   483    $ Water

595   3   0.10018       1   -2     4  -484                      $ Water Hole

596   3   0.10018       1   -2     4   484  -485                $ Water Hole

597   3   0.10018       1   -2     4    16    57   -58   485    $ Water Hole

598   1   0.068525      1   -2  -486                            $ Fuel

599   2   0.055323      1   -2   486  -487                      $ Clad

600   3   0.10018       1   -2    16   -17    58   -59   487    $ Water

601   1   0.068525      1   -2  -488                            $ Fuel

602   2   0.055323      1   -2   488  -489                      $ Clad

603   3   0.10018       1   -2    16   -17    59   -60   489    $ Water

604   1   0.068525      1   -2  -490                            $ Fuel

605   2   0.055323      1   -2   490  -491                      $ Clad

606   3   0.10018       1   -2    16   -17    60   -61   491    $ Water

607   1   0.068525      1   -2  -492                            $ Fuel

608   2   0.055323      1   -2   492  -493                      $ Clad

609   3   0.10018       1   -2    16   -17    61   -62   493    $ Water

610   1   0.068525      1   -2  -494                            $ Fuel

611   2   0.055323      1   -2   494  -495                      $ Clad

612   3   0.10018       1   -2    16   -17    62   -63   495    $ Water

613   1   0.068525      1   -2  -496                            $ Fuel

614   2   0.055323      1   -2   496  -497                      $ Clad

615   3   0.10018       1   -2    16   -17    63   -64   497    $ Water

616   1   0.068525      1   -2  -498                            $ Fuel

617   2   0.055323      1   -2   498  -499                      $ Clad

618   3   0.10018       1   -2    16   -17    64   -65   499    $ Water

619   3   0.10018       1   -2  -500                            $ Water Hole

620   3   0.10018       1   -2   500  -501                      $ Water Hole

621   3   0.10018       1   -2    16   -17    65   -66   501    $ Water Hole

622   1   0.068525      1   -2  -502                            $ Fuel

623   2   0.055323      1   -2   502  -503                      $ Clad

624   3   0.10018       1   -2    16   -17    66   -67   503    $ Water

625   1   0.068525      1   -2  -504                            $ Fuel

626   2   0.055323      1   -2   504  -505                      $ Clad

627   3   0.10018       1   -2    16   -17    67   -68   505    $ Water

628   1   0.068525      1   -2  -506                            $ Fuel

629   2   0.055323      1   -2   506  -507                      $ Clad

630   3   0.10018       1   -2    16   -17    68   -69   507    $ Water

631   1   0.068525      1   -2     4  -508                      $ Fuel

632   2   0.055323      1   -2     4   508  -509                $ Clad

633   3   0.10018       1   -2     4    17    58   -59   509    $ Water

634   1   0.068525      1   -2  -510                            $ Fuel

635   2   0.055323      1   -2   510  -511                      $ Clad

636   3   0.10018       1   -2    17   -18    59   -60   511    $ Water

637   1   0.068525      1   -2  -512                            $ Fuel

638   2   0.055323      1   -2   512  -513                      $ Clad

639   3   0.10018       1   -2    17   -18    60   -61   513    $ Water

640   1   0.068525      1   -2  -514                            $ Fuel

641   2   0.055323      1   -2   514  -515                      $ Clad

642   3   0.10018       1   -2    17   -18    61   -62   515    $ Water

643   1   0.068525      1   -2  -516                            $ Fuel

644   2   0.055323      1   -2   516  -517                      $ Clad

645   3   0.10018       1   -2    17   -18    62   -63   517    $ Water

646   1   0.068525      1   -2  -518                            $ Fuel

647   2   0.055323      1   -2   518  -519                      $ Clad

648   3   0.10018       1   -2    17   -18    63   -64   519    $ Water

649   1   0.068525      1   -2  -520                            $ Fuel

650   2   0.055323      1   -2   520  -521                      $ Clad

651   3   0.10018       1   -2    17   -18    64   -65   521    $ Water

652   1   0.068525      1   -2  -522                            $ Fuel

653   2   0.055323      1   -2   522  -523                      $ Clad

654   3   0.10018       1   -2    17   -18    65   -66   523    $ Water

655   1   0.068525      1   -2  -524                            $ Fuel

656   2   0.055323      1   -2   524  -525                      $ Clad

657   3   0.10018       1   -2    17   -18    66   -67   525    $ Water

658   1   0.068525      1   -2  -526                            $ Fuel

659   2   0.055323      1   -2   526  -527                      $ Clad

660   3   0.10018       1   -2    17   -18    67   -68   527    $ Water

661   1   0.068525      1   -2  -528                            $ Fuel

662   2   0.055323      1   -2   528  -529                      $ Clad

663   3   0.10018       1   -2    17   -18    68   -69   529    $ Water

664   3   0.10018       1   -2     4  -530                      $ Water Hole

665   3   0.10018       1   -2     4   530  -531                $ Water Hole

666   3   0.10018       1   -2     4    18    59   -60   531    $ Water Hole

667   1   0.068525      1   -2  -532                            $ Fuel

668   2   0.055323      1   -2   532  -533                      $ Clad

669   3   0.10018       1   -2    18   -19    60   -61   533    $ Water

670   1   0.068525      1   -2  -534                            $ Fuel

671   2   0.055323      1   -2   534  -535                      $ Clad

672   3   0.10018       1   -2    18   -19    61   -62   535    $ Water

673   1   0.068525      1   -2  -536                            $ Fuel

674   2   0.055323      1   -2   536  -537                      $ Clad

675   3   0.10018       1   -2    18   -19    62   -63   537    $ Water

676   3   0.10018       1   -2  -538                            $ Water Hole

677   3   0.10018       1   -2   538  -539                      $ Water Hole

678   3   0.10018       1   -2    18   -19    63   -64   539    $ Water Hole

679   1   0.068525      1   -2  -540                            $ Fuel

680   2   0.055323      1   -2   540  -541                      $ Clad

681   3   0.10018       1   -2    18   -19    64   -65   541    $ Water

682   1   0.068525      1   -2  -542                            $ Fuel

683   2   0.055323      1   -2   542  -543                      $ Clad

684   3   0.10018       1   -2    18   -19    65   -66   543    $ Water

685   3   0.10018       1   -2  -544                            $ Water Hole

686   3   0.10018       1   -2   544  -545                      $ Water Hole

687   3   0.10018       1   -2    18   -19    66   -67   545    $ Water Hole

688   1   0.068525      1   -2  -546                            $ Fuel

689   2   0.055323      1   -2   546  -547                      $ Clad

690   3   0.10018       1   -2    18   -19    67   -68   547    $ Water

691   1   0.068525      1   -2  -548                            $ Fuel

692   2   0.055323      1   -2   548  -549                      $ Clad

693   3   0.10018       1   -2    18   -19    68   -69   549    $ Water

694   1   0.068525      1   -2     4  -550                      $ Fuel

695   2   0.055323      1   -2     4   550  -551                $ Clad

696   3   0.10018       1   -2     4    19    60   -61   551    $ Water

697   1   0.068525      1   -2  -552                            $ Fuel

698   2   0.055323      1   -2   552  -553                      $ Clad

699   3   0.10018       1   -2    19   -20    61   -62   553    $ Water

700   1   0.068525      1   -2  -554                            $ Fuel

701   2   0.055323      1   -2   554  -555                      $ Clad

702   3   0.10018       1   -2    19   -20    62   -63   555    $ Water

703   1   0.068525      1   -2  -556                            $ Fuel

704   2   0.055323      1   -2   556  -557                      $ Clad

705   3   0.10018       1   -2    19   -20    63   -64   557    $ Water

706   1   0.068525      1   -2  -558                            $ Fuel

707   2   0.055323      1   -2   558  -559                      $ Clad

708   3   0.10018       1   -2    19   -20    64   -65   559    $ Water

709   1   0.068525      1   -2  -560                            $ Fuel

710   2   0.055323      1   -2   560  -561                      $ Clad

711   3   0.10018       1   -2    19   -20    65   -66   561    $ Water

712   1   0.068525      1   -2  -562                            $ Fuel

713   2   0.055323      1   -2   562  -563                      $ Clad

714   3   0.10018       1   -2    19   -20    66   -67   563    $ Water

715   1   0.068525      1   -2  -564                            $ Fuel

716   2   0.055323      1   -2   564  -565                      $ Clad

717   3   0.10018       1   -2    19   -20    67   -68   565    $ Water

718   1   0.068525      1   -2  -566                            $ Fuel

719   2   0.055323      1   -2   566  -567                      $ Clad

720   3   0.10018       1   -2    19   -20    68   -69   567    $ Water

721   3   0.10018       1   -2     4  -568                      $ Water Hole

722   3   0.10018       1   -2     4   568  -569                $ Water Hole

723   3   0.10018       1   -2     4    20    61   -62   569    $ Water Hole

724   1   0.068525      1   -2  -570                            $ Fuel

725   2   0.055323      1   -2   570  -571                      $ Clad

726   3   0.10018       1   -2    20   -21    62   -63   571    $ Water

727   1   0.068525      1   -2  -572                            $ Fuel

728   2   0.055323      1   -2   572  -573                      $ Clad

729   3   0.10018       1   -2    20   -21    63   -64   573    $ Water

730   1   0.068525      1   -2  -574                            $ Fuel

731   2   0.055323      1   -2   574  -575                      $ Clad

732   3   0.10018       1   -2    20   -21    64   -65   575    $ Water

733   1   0.068525      1   -2  -576                            $ Fuel

734   2   0.055323      1   -2   576  -577                      $ Clad

735   3   0.10018       1   -2    20   -21    65   -66   577    $ Water

736   1   0.068525      1   -2  -578                            $ Fuel

737   2   0.055323      1   -2   578  -579                      $ Clad

738   3   0.10018       1   -2    20   -21    66   -67   579    $ Water

739   1   0.068525      1   -2  -580                            $ Fuel

740   2   0.055323      1   -2   580  -581                      $ Clad

741   3   0.10018       1   -2    20   -21    67   -68   581    $ Water

742   1   0.068525      1   -2  -582                            $ Fuel

743   2   0.055323      1   -2   582  -583                      $ Clad

744   3   0.10018       1   -2    20   -21    68   -69   583    $ Water

745   1   0.068525      1   -2     4  -584                      $ Fuel

746   2   0.055323      1   -2     4   584  -585                $ Clad

747   3   0.10018       1   -2     4    21    62   -63   585    $ Water

748   1   0.068525      1   -2  -586                            $ Fuel

749   2   0.055323      1   -2   586  -587                      $ Clad

750   3   0.10018       1   -2    21   -22    63   -64   587    $ Water

751   1   0.068525      1   -2  -588                            $ Fuel

752   2   0.055323      1   -2   588  -589                      $ Clad

753   3   0.10018       1   -2    21   -22    64   -65   589    $ Water

754   1   0.068525      1   -2  -590                            $ Fuel

755   2   0.055323      1   -2   590  -591                      $ Clad

756   3   0.10018       1   -2    21   -22    65   -66   591    $ Water

757   1   0.068525      1   -2  -592                            $ Fuel

758   2   0.055323      1   -2   592  -593                      $ Clad

759   3   0.10018       1   -2    21   -22    66   -67   593    $ Water

760   1   0.068525      1   -2  -594                            $ Fuel

761   2   0.055323      1   -2   594  -595                      $ Clad

762   3   0.10018       1   -2    21   -22    67   -68   595    $ Water

763   1   0.068525      1   -2  -596                            $ Fuel

764   2   0.055323      1   -2   596  -597                      $ Clad

765   3   0.10018       1   -2    21   -22    68   -69   597    $ Water

766   3   0.10018       1   -2     4  -598                      $ Water Hole

767   3   0.10018       1   -2     4   598  -599                $ Water Hole

768   3   0.10018       1   -2     4    22    63   -64   599    $ Water Hole

769   1   0.068525      1   -2  -600                            $ Fuel

770   2   0.055323      1   -2   600  -601                      $ Clad

771   3   0.10018       1   -2    22   -23    64   -65   601    $ Water

772   1   0.068525      1   -2  -602                            $ Fuel

773   2   0.055323      1   -2   602  -603                      $ Clad

774   3   0.10018       1   -2    22   -23    65   -66   603    $ Water

775   3   0.10018       1   -2  -604                            $ Water Hole

776   3   0.10018       1   -2   604  -605                      $ Water Hole

777   3   0.10018       1   -2    22   -23    66   -67   605    $ Water Hole

778   1   0.068525      1   -2  -606                            $ Fuel

779   2   0.055323      1   -2   606  -607                      $ Clad

780   3   0.10018       1   -2    22   -23    67   -68   607    $ Water

781   1   0.068525      1   -2  -608                            $ Fuel

782   2   0.055323      1   -2   608  -609                      $ Clad

783   3   0.10018       1   -2    22   -23    68   -69   609    $ Water

784   1   0.068525      1   -2     4  -610                      $ Fuel

785   2   0.055323      1   -2     4   610  -611                $ Clad

786   3   0.10018       1   -2     4    23    64   -65   611    $ Water

787   1   0.068525      1   -2  -612                            $ Fuel

788   2   0.055323      1   -2   612  -613                      $ Clad

789   3   0.10018       1   -2    23   -24    65   -66   613    $ Water

790   1   0.068525      1   -2  -614                            $ Fuel

791   2   0.055323      1   -2   614  -615                      $ Clad

792   3   0.10018       1   -2    23   -24    66   -67   615    $ Water

793   1   0.068525      1   -2  -616                            $ Fuel

794   2   0.055323      1   -2   616  -617                      $ Clad

795   3   0.10018       1   -2    23   -24    67   -68   617    $ Water

796   1   0.068525      1   -2  -618                            $ Fuel

797   2   0.055323      1   -2   618  -619                      $ Clad

798   3   0.10018       1   -2    23   -24    68   -69   619    $ Water

799   3   0.10018       1   -2     4  -620                      $ Water Hole

800   3   0.10018       1   -2     4   620  -621                $ Water Hole

801   3   0.10018       1   -2     4    24    65   -66   621    $ Water Hole

802   1   0.068525      1   -2  -622                            $ Fuel

803   2   0.055323      1   -2   622  -623                      $ Clad

804   3   0.10018       1   -2    24   -25    66   -67   623    $ Water

805   1   0.068525      1   -2  -624                            $ Fuel

806   2   0.055323      1   -2   624  -625                      $ Clad

807   3   0.10018       1   -2    24   -25    67   -68   625    $ Water

808   1   0.068525      1   -2  -626                            $ Fuel

809   2   0.055323      1   -2   626  -627                      $ Clad

810   3   0.10018       1   -2    24   -25    68   -69   627    $ Water

811   1   0.068525      1   -2     4  -628                      $ Fuel

812   2   0.055323      1   -2     4   628  -629                $ Clad

813   3   0.10018       1   -2     4    25    66   -67   629    $ Water

814   1   0.068525      1   -2  -630                            $ Fuel

815   2   0.055323      1   -2   630  -631                      $ Clad

816   3   0.10018       1   -2    25   -26    67   -68   631    $ Water

817   1   0.068525      1   -2  -632                            $ Fuel

818   2   0.055323      1   -2   632  -633                      $ Clad

819   3   0.10018       1   -2    25   -26    68   -69   633    $ Water

820   1   0.068525      1   -2     4  -634                      $ Fuel

821   2   0.055323      1   -2     4   634  -635                $ Clad

822   3   0.10018       1   -2     4    26    67   -68   635    $ Water

823   1   0.068525      1   -2  -636                            $ Fuel

824   2   0.055323      1   -2   636  -637                      $ Clad

825   3   0.10018       1   -2    26   -27    68   -69   637    $ Water

826   1   0.068525      1   -2     4  -638                      $ Fuel

827   2   0.055323      1   -2     4   638  -639                $ Clad

828   3   0.10018       1   -2     4    27    68   -69   639    $ Water

c    Buffer Cells and Reflector

829   1   0.068525      1   -2     3  -640                      $ Fuel

830   2   0.055323      1   -2     3   640  -641                $ Clad

831   3   0.10018       1   -2     3    -6    69   -70   641    $ Water

832   1   0.068525      1   -2     3  -642                      $ Fuel

833   2   0.055323      1   -2     3   642  -643                $ Clad

834   3   0.10018       1   -2     3    -6    70   -71   643    $ Water

835   1   0.068525      1   -2     3  -644                      $ Fuel

836   2   0.055323      1   -2     3   644  -645                $ Clad

837   3   0.10018       1   -2     3    -6    71   -72   645    $ Water

838   1   0.068525      1   -2     3  -646                      $ Fuel

839   2   0.055323      1   -2     3   646  -647                $ Clad

840   3   0.10018       1   -2     3    -6    72   -73   647    $ Water

841   1   0.068525      1   -2     3  -648                      $ Fuel

842   2   0.055323      1   -2     3   648  -649                $ Clad

843   3   0.10018       1   -2     3    -6    73   -74   649    $ Water

844   1   0.068525      1   -2     3  -650                      $ Fuel

845   2   0.055323      1   -2     3   650  -651                $ Clad

846   3   0.10018       1   -2     3    -6    74   -75   651    $ Water

847   1   0.068525      1   -2     3  -652                      $ Fuel

848   2   0.055323      1   -2     3   652  -653                $ Clad

849   3   0.10018       1   -2     3    -6    75   -76   653    $ Water

850   1   0.068525      1   -2     3  -654                      $ Fuel

851   2   0.055323      1   -2     3   654  -655                $ Clad

852   3   0.10018       1   -2     3    -6    76   -77   655    $ Water

853   1   0.068525      1   -2     3  -656                      $ Fuel

854   2   0.055323      1   -2     3   656  -657                $ Clad

855   3   0.10018       1   -2     3    -6    77   -78   657    $ Water

856   1   0.068525      1   -2     3  -658                      $ Fuel

857   2   0.055323      1   -2     3   658  -659                $ Clad

858   3   0.10018       1   -2     3    -6    78   -79   659    $ Water

859   1   0.068525      1   -2     3  -660                      $ Fuel

860   2   0.055323      1   -2     3   660  -661                $ Clad

861   3   0.10018       1   -2     3    -6    79   -80   661    $ Water

862   1   0.068525      1   -2     3  -662                      $ Fuel

863   2   0.055323      1   -2     3   662  -663                $ Clad

864   3   0.10018       1   -2     3    -6    80   -81   663    $ Water

865   1   0.068525      1   -2     3  -664                      $ Fuel

866   2   0.055323      1   -2     3   664  -665                $ Clad

867   3   0.10018       1   -2     3    -6    81   -82   665    $ Water

868   1   0.068525      1   -2     3  -666                      $ Fuel

869   2   0.055323      1   -2     3   666  -667                $ Clad

870   3   0.10018       1   -2     3    -6    82   -83   667    $ Water

871   1   0.068525      1   -2     3  -668                      $ Fuel

872   2   0.055323      1   -2     3   668  -669                $ Clad

873   3   0.10018       1   -2     3    -6    83   -84   669    $ Water

874   1   0.068525      1   -2     3  -670                      $ Fuel

875   2   0.055323      1   -2     3   670  -671                $ Clad

876   3   0.10018       1   -2     3    -6    84   -85   671    $ Water

877   1   0.068525      1   -2     3  -672                      $ Fuel

878   2   0.055323      1   -2     3   672  -673                $ Clad

879   3   0.10018       1   -2     3    -6    85   -86   673    $ Water

880   1   0.068525      1   -2     3  -674                      $ Fuel

881   2   0.055323      1   -2     3   674  -675                $ Clad

882   3   0.10018       1   -2     3    -6    86   -87   675    $ Water

883   3   0.10018       1   -2     3    -6    87    -5          $ Reflector

884   1   0.068525      1   -2  -676                            $ Fuel

885   2   0.055323      1   -2   676  -677                      $ Clad

886   3   0.10018       1   -2     6    -7    69   -70   677    $ Water

887   1   0.068525      1   -2  -678                            $ Fuel

888   2   0.055323      1   -2   678  -679                      $ Clad

889   3   0.10018       1   -2     6    -7    70   -71   679    $ Water

890   1   0.068525      1   -2  -680                            $ Fuel

891   2   0.055323      1   -2   680  -681                      $ Clad

892   3   0.10018       1   -2     6    -7    71   -72   681    $ Water

893   1   0.068525      1   -2  -682                            $ Fuel

894   2   0.055323      1   -2   682  -683                      $ Clad

895   3   0.10018       1   -2     6    -7    72   -73   683    $ Water

896   1   0.068525      1   -2  -684                            $ Fuel

897   2   0.055323      1   -2   684  -685                      $ Clad

898   3   0.10018       1   -2     6    -7    73   -74   685    $ Water

899   1   0.068525      1   -2  -686                            $ Fuel

900   2   0.055323      1   -2   686  -687                      $ Clad

901   3   0.10018       1   -2     6    -7    74   -75   687    $ Water

902   1   0.068525      1   -2  -688                            $ Fuel

903   2   0.055323      1   -2   688  -689                      $ Clad

904   3   0.10018       1   -2     6    -7    75   -76   689    $ Water

905   1   0.068525      1   -2  -690                            $ Fuel

906   2   0.055323      1   -2   690  -691                      $ Clad

907   3   0.10018       1   -2     6    -7    76   -77   691    $ Water

908   1   0.068525      1   -2  -692                            $ Fuel

909   2   0.055323      1   -2   692  -693                      $ Clad

910   3   0.10018       1   -2     6    -7    77   -78   693    $ Water

911   1   0.068525      1   -2  -694                            $ Fuel

912   2   0.055323      1   -2   694  -695                      $ Clad

913   3   0.10018       1   -2     6    -7    78   -79   695    $ Water

914   1   0.068525      1   -2  -696                            $ Fuel

915   2   0.055323      1   -2   696  -697                      $ Clad

916   3   0.10018       1   -2     6    -7    79   -80   697    $ Water

917   1   0.068525      1   -2  -698                            $ Fuel

918   2   0.055323      1   -2   698  -699                      $ Clad

919   3   0.10018       1   -2     6    -7    80   -81   699    $ Water

920   1   0.068525      1   -2  -700                            $ Fuel

921   2   0.055323      1   -2   700  -701                      $ Clad

922   3   0.10018       1   -2     6    -7    81   -82   701    $ Water

923   1   0.068525      1   -2  -702                            $ Fuel

924   2   0.055323      1   -2   702  -703                      $ Clad

925   3   0.10018       1   -2     6    -7    82   -83   703    $ Water

926   1   0.068525      1   -2  -704                            $ Fuel

927   2   0.055323      1   -2   704  -705                      $ Clad

928   3   0.10018       1   -2     6    -7    83   -84   705    $ Water

929   1   0.068525      1   -2  -706                            $ Fuel

930   2   0.055323      1   -2   706  -707                      $ Clad

931   3   0.10018       1   -2     6    -7    84   -85   707    $ Water

932   1   0.068525      1   -2  -708                            $ Fuel

933   2   0.055323      1   -2   708  -709                      $ Clad

934   3   0.10018       1   -2     6    -7    85   -86   709    $ Water

935   1   0.068525      1   -2  -710                            $ Fuel

936   2   0.055323      1   -2   710  -711                      $ Clad

937   3   0.10018       1   -2     6    -7    86   -87   711    $ Water

938   3   0.10018       1   -2     6    -7    87    -5          $ Reflector

939   1   0.068525      1   -2  -712                            $ Fuel

940   2   0.055323      1   -2   712  -713                      $ Clad

941   3   0.10018       1   -2     7    -8    69   -70   713    $ Water

942   1   0.068525      1   -2  -714                            $ Fuel

943   2   0.055323      1   -2   714  -715                      $ Clad

944   3   0.10018       1   -2     7    -8    70   -71   715    $ Water

945   1   0.068525      1   -2  -716                            $ Fuel

946   2   0.055323      1   -2   716  -717                      $ Clad

947   3   0.10018       1   -2     7    -8    71   -72   717    $ Water

948   1   0.068525      1   -2  -718                            $ Fuel

949   2   0.055323      1   -2   718  -719                      $ Clad

950   3   0.10018       1   -2     7    -8    72   -73   719    $ Water

951   1   0.068525      1   -2  -720                            $ Fuel

952   2   0.055323      1   -2   720  -721                      $ Clad

953   3   0.10018       1   -2     7    -8    73   -74   721    $ Water

954   1   0.068525      1   -2  -722                            $ Fuel

955   2   0.055323      1   -2   722  -723                      $ Clad

956   3   0.10018       1   -2     7    -8    74   -75   723    $ Water

957   1   0.068525      1   -2  -724                            $ Fuel

958   2   0.055323      1   -2   724  -725                      $ Clad

959   3   0.10018       1   -2     7    -8    75   -76   725    $ Water

960   1   0.068525      1   -2  -726                            $ Fuel

961   2   0.055323      1   -2   726  -727                      $ Clad

962   3   0.10018       1   -2     7    -8    76   -77   727    $ Water

963   1   0.068525      1   -2  -728                            $ Fuel

964   2   0.055323      1   -2   728  -729                      $ Clad

965   3   0.10018       1   -2     7    -8    77   -78   729    $ Water

966   1   0.068525      1   -2  -730                            $ Fuel

967   2   0.055323      1   -2   730  -731                      $ Clad

968   3   0.10018       1   -2     7    -8    78   -79   731    $ Water

969   1   0.068525      1   -2  -732                            $ Fuel

970   2   0.055323      1   -2   732  -733                      $ Clad

971   3   0.10018       1   -2     7    -8    79   -80   733    $ Water

972   1   0.068525      1   -2  -734                            $ Fuel

973   2   0.055323      1   -2   734  -735                      $ Clad

974   3   0.10018       1   -2     7    -8    80   -81   735    $ Water

975   1   0.068525      1   -2  -736                            $ Fuel

976   2   0.055323      1   -2   736  -737                      $ Clad

977   3   0.10018       1   -2     7    -8    81   -82   737    $ Water

978   1   0.068525      1   -2  -738                            $ Fuel

979   2   0.055323      1   -2   738  -739                      $ Clad

980   3   0.10018       1   -2     7    -8    82   -83   739    $ Water

981   1   0.068525      1   -2  -740                            $ Fuel

982   2   0.055323      1   -2   740  -741                      $ Clad

983   3   0.10018       1   -2     7    -8    83   -84   741    $ Water

984   1   0.068525      1   -2  -742                            $ Fuel

985   2   0.055323      1   -2   742  -743                      $ Clad

986   3   0.10018       1   -2     7    -8    84   -85   743    $ Water

987   1   0.068525      1   -2  -744                            $ Fuel

988   2   0.055323      1   -2   744  -745                      $ Clad

989   3   0.10018       1   -2     7    -8    85   -86   745    $ Water

990   1   0.068525      1   -2  -746                            $ Fuel

991   2   0.055323      1   -2   746  -747                      $ Clad

992   3   0.10018       1   -2     7    -8    86   -87   747    $ Water

993   3   0.10018       1   -2     7    -8    87    -5          $ Reflector

994   1   0.068525      1   -2  -748                            $ Fuel

995   2   0.055323      1   -2   748  -749                      $ Clad

996   3   0.10018       1   -2     8    -9    69   -70   749    $ Water

997   1   0.068525      1   -2  -750                            $ Fuel

998   2   0.055323      1   -2   750  -751                      $ Clad

999   3   0.10018       1   -2     8    -9    70   -71   751    $ Water

1000  1   0.068525      1   -2  -752                            $ Fuel

1001  2   0.055323      1   -2   752  -753                      $ Clad

1002  3   0.10018       1   -2     8    -9    71   -72   753    $ Water

1003  1   0.068525      1   -2  -754                            $ Fuel

1004  2   0.055323      1   -2   754  -755                      $ Clad

1005  3   0.10018       1   -2     8    -9    72   -73   755    $ Water

1006  1   0.068525      1   -2  -756                            $ Fuel

1007  2   0.055323      1   -2   756  -757                      $ Clad

1008  3   0.10018       1   -2     8    -9    73   -74   757    $ Water

1009  1   0.068525      1   -2  -758                            $ Fuel

1010  2   0.055323      1   -2   758  -759                      $ Clad

1011  3   0.10018       1   -2     8    -9    74   -75   759    $ Water

1012  1   0.068525      1   -2  -760                            $ Fuel

1013  2   0.055323      1   -2   760  -761                      $ Clad

1014  3   0.10018       1   -2     8    -9    75   -76   761    $ Water

1015  1   0.068525      1   -2  -762                            $ Fuel

1016  2   0.055323      1   -2   762  -763                      $ Clad

1017  3   0.10018       1   -2     8    -9    76   -77   763    $ Water

1018  1   0.068525      1   -2  -764                            $ Fuel

1019  2   0.055323      1   -2   764  -765                      $ Clad

1020  3   0.10018       1   -2     8    -9    77   -78   765    $ Water

1021  1   0.068525      1   -2  -766                            $ Fuel

1022  2   0.055323      1   -2   766  -767                      $ Clad

1023  3   0.10018       1   -2     8    -9    78   -79   767    $ Water

1024  1   0.068525      1   -2  -768                            $ Fuel

1025  2   0.055323      1   -2   768  -769                      $ Clad

1026  3   0.10018       1   -2     8    -9    79   -80   769    $ Water

1027  1   0.068525      1   -2  -770                            $ Fuel

1028  2   0.055323      1   -2   770  -771                      $ Clad

1029  3   0.10018       1   -2     8    -9    80   -81   771    $ Water

1030  1   0.068525      1   -2  -772                            $ Fuel

1031  2   0.055323      1   -2   772  -773                      $ Clad

1032  3   0.10018       1   -2     8    -9    81   -82   773    $ Water

1033  1   0.068525      1   -2  -774                            $ Fuel

1034  2   0.055323      1   -2   774  -775                      $ Clad

1035  3   0.10018       1   -2     8    -9    82   -83   775    $ Water

1036  1   0.068525      1   -2  -776                            $ Fuel

1037  2   0.055323      1   -2   776  -777                      $ Clad

1038  3   0.10018       1   -2     8    -9    83   -84   777    $ Water

1039  1   0.068525      1   -2  -778                            $ Fuel

1040  2   0.055323      1   -2   778  -779                      $ Clad

1041  3   0.10018       1   -2     8    -9    84   -85   779    $ Water

1042  1   0.068525      1   -2  -780                            $ Fuel

1043  2   0.055323      1   -2   780  -781                      $ Clad

1044  3   0.10018       1   -2     8    -9    85   -86   781    $ Water

1045  1   0.068525      1   -2  -782                            $ Fuel

1046  2   0.055323      1   -2   782  -783                      $ Clad

1047  3   0.10018       1   -2     8    -9    86   -87   783    $ Water

1048  3   0.10018       1   -2     8    -9    87    -5          $ Reflector

1049  1   0.068525      1   -2  -784                            $ Fuel

1050  2   0.055323      1   -2   784  -785                      $ Clad

1051  3   0.10018       1   -2     9   -10    69   -70   785    $ Water

1052  1   0.068525      1   -2  -786                            $ Fuel

1053  2   0.055323      1   -2   786  -787                      $ Clad

1054  3   0.10018       1   -2     9   -10    70   -71   787    $ Water

1055  1   0.068525      1   -2  -788                            $ Fuel

1056  2   0.055323      1   -2   788  -789                      $ Clad

1057  3   0.10018       1   -2     9   -10    71   -72   789    $ Water

1058  1   0.068525      1   -2  -790                            $ Fuel

1059  2   0.055323      1   -2   790  -791                      $ Clad

1060  3   0.10018       1   -2     9   -10    72   -73   791    $ Water

1061  1   0.068525      1   -2  -792                            $ Fuel

1062  2   0.055323      1   -2   792  -793                      $ Clad

1063  3   0.10018       1   -2     9   -10    73   -74   793    $ Water

1064  1   0.068525      1   -2  -794                            $ Fuel

1065  2   0.055323      1   -2   794  -795                      $ Clad

1066  3   0.10018       1   -2     9   -10    74   -75   795    $ Water

1067  1   0.068525      1   -2  -796                            $ Fuel

1068  2   0.055323      1   -2   796  -797                      $ Clad

1069  3   0.10018       1   -2     9   -10    75   -76   797    $ Water

1070  1   0.068525      1   -2  -798                            $ Fuel

1071  2   0.055323      1   -2   798  -799                      $ Clad

1072  3   0.10018       1   -2     9   -10    76   -77   799    $ Water

1073  1   0.068525      1   -2  -800                            $ Fuel

1074  2   0.055323      1   -2   800  -801                      $ Clad

1075  3   0.10018       1   -2     9   -10    77   -78   801    $ Water

1076  1   0.068525      1   -2  -802                            $ Fuel

1077  2   0.055323      1   -2   802  -803                      $ Clad

1078  3   0.10018       1   -2     9   -10    78   -79   803    $ Water

1079  1   0.068525      1   -2  -804                            $ Fuel

1080  2   0.055323      1   -2   804  -805                      $ Clad

1081  3   0.10018       1   -2     9   -10    79   -80   805    $ Water

1082  1   0.068525      1   -2  -806                            $ Fuel

1083  2   0.055323      1   -2   806  -807                      $ Clad

1084  3   0.10018       1   -2     9   -10    80   -81   807    $ Water

1085  1   0.068525      1   -2  -808                            $ Fuel

1086  2   0.055323      1   -2   808  -809                      $ Clad

1087  3   0.10018       1   -2     9   -10    81   -82   809    $ Water

1088  1   0.068525      1   -2  -810                            $ Fuel

1089  2   0.055323      1   -2   810  -811                      $ Clad

1090  3   0.10018       1   -2     9   -10    82   -83   811    $ Water

1091  1   0.068525      1   -2  -812                            $ Fuel

1092  2   0.055323      1   -2   812  -813                      $ Clad

1093  3   0.10018       1   -2     9   -10    83   -84   813    $ Water

1094  1   0.068525      1   -2  -814                            $ Fuel

1095  2   0.055323      1   -2   814  -815                      $ Clad

1096  3   0.10018       1   -2     9   -10    84   -85   815    $ Water

1097  1   0.068525      1   -2  -816                            $ Fuel

1098  2   0.055323      1   -2   816  -817                      $ Clad

1099  3   0.10018       1   -2     9   -10    85   -86   817    $ Water

1100  1   0.068525      1   -2  -818                            $ Fuel

1101  2   0.055323      1   -2   818  -819                      $ Clad

1102  3   0.10018       1   -2     9   -10    86   -87   819    $ Water

1103  3   0.10018       1   -2     9   -10    87    -5          $ Reflector

1104  1   0.068525      1   -2  -820                            $ Fuel

1105  2   0.055323      1   -2   820  -821                      $ Clad

1106  3   0.10018       1   -2    10   -11    69   -70   821    $ Water

1107  1   0.068525      1   -2  -822                            $ Fuel

1108  2   0.055323      1   -2   822  -823                      $ Clad

1109  3   0.10018       1   -2    10   -11    70   -71   823    $ Water

1110  1   0.068525      1   -2  -824                            $ Fuel

1111  2   0.055323      1   -2   824  -825                      $ Clad

1112  3   0.10018       1   -2    10   -11    71   -72   825    $ Water

1113  1   0.068525      1   -2  -826                            $ Fuel

1114  2   0.055323      1   -2   826  -827                      $ Clad

1115  3   0.10018       1   -2    10   -11    72   -73   827    $ Water

1116  1   0.068525      1   -2  -828                            $ Fuel

1117  2   0.055323      1   -2   828  -829                      $ Clad

1118  3   0.10018       1   -2    10   -11    73   -74   829    $ Water

1119  1   0.068525      1   -2  -830                            $ Fuel

1120  2   0.055323      1   -2   830  -831                      $ Clad

1121  3   0.10018       1   -2    10   -11    74   -75   831    $ Water

1122  1   0.068525      1   -2  -832                            $ Fuel

1123  2   0.055323      1   -2   832  -833                      $ Clad

1124  3   0.10018       1   -2    10   -11    75   -76   833    $ Water

1125  1   0.068525      1   -2  -834                            $ Fuel

1126  2   0.055323      1   -2   834  -835                      $ Clad

1127  3   0.10018       1   -2    10   -11    76   -77   835    $ Water

1128  1   0.068525      1   -2  -836                            $ Fuel

1129  2   0.055323      1   -2   836  -837                      $ Clad

1130  3   0.10018       1   -2    10   -11    77   -78   837    $ Water

1131  1   0.068525      1   -2  -838                            $ Fuel

1132  2   0.055323      1   -2   838  -839                      $ Clad

1133  3   0.10018       1   -2    10   -11    78   -79   839    $ Water

1134  1   0.068525      1   -2  -840                            $ Fuel

1135  2   0.055323      1   -2   840  -841                      $ Clad

1136  3   0.10018       1   -2    10   -11    79   -80   841    $ Water

1137  1   0.068525      1   -2  -842                            $ Fuel

1138  2   0.055323      1   -2   842  -843                      $ Clad

1139  3   0.10018       1   -2    10   -11    80   -81   843    $ Water

1140  1   0.068525      1   -2  -844                            $ Fuel

1141  2   0.055323      1   -2   844  -845                      $ Clad

1142  3   0.10018       1   -2    10   -11    81   -82   845    $ Water

1143  1   0.068525      1   -2  -846                            $ Fuel

1144  2   0.055323      1   -2   846  -847                      $ Clad

1145  3   0.10018       1   -2    10   -11    82   -83   847    $ Water

1146  1   0.068525      1   -2  -848                            $ Fuel

1147  2   0.055323      1   -2   848  -849                      $ Clad

1148  3   0.10018       1   -2    10   -11    83   -84   849    $ Water

1149  1   0.068525      1   -2  -850                            $ Fuel

1150  2   0.055323      1   -2   850  -851                      $ Clad

1151  3   0.10018       1   -2    10   -11    84   -85   851    $ Water

1152  1   0.068525      1   -2  -852                            $ Fuel

1153  2   0.055323      1   -2   852  -853                      $ Clad

1154  3   0.10018       1   -2    10   -11    85   -86   853    $ Water

1155  1   0.068525      1   -2  -854                            $ Fuel

1156  2   0.055323      1   -2   854  -855                      $ Clad

1157  3   0.10018       1   -2    10   -11    86   -87   855    $ Water

1158  3   0.10018       1   -2    10   -11    87    -5          $ Reflector

1159  1   0.068525      1   -2  -856                            $ Fuel

1160  2   0.055323      1   -2   856  -857                      $ Clad

1161  3   0.10018       1   -2    11   -12    69   -70   857    $ Water

1162  1   0.068525      1   -2  -858                            $ Fuel

1163  2   0.055323      1   -2   858  -859                      $ Clad

1164  3   0.10018       1   -2    11   -12    70   -71   859    $ Water

1165  1   0.068525      1   -2  -860                            $ Fuel

1166  2   0.055323      1   -2   860  -861                      $ Clad

1167  3   0.10018       1   -2    11   -12    71   -72   861    $ Water

1168  1   0.068525      1   -2  -862                            $ Fuel

1169  2   0.055323      1   -2   862  -863                      $ Clad

1170  3   0.10018       1   -2    11   -12    72   -73   863    $ Water

1171  1   0.068525      1   -2  -864                            $ Fuel

1172  2   0.055323      1   -2   864  -865                      $ Clad

1173  3   0.10018       1   -2    11   -12    73   -74   865    $ Water

1174  1   0.068525      1   -2  -866                            $ Fuel

1175  2   0.055323      1   -2   866  -867                      $ Clad

1176  3   0.10018       1   -2    11   -12    74   -75   867    $ Water

1177  1   0.068525      1   -2  -868                            $ Fuel

1178  2   0.055323      1   -2   868  -869                      $ Clad

1179  3   0.10018       1   -2    11   -12    75   -76   869    $ Water

1180  1   0.068525      1   -2  -870                            $ Fuel

1181  2   0.055323      1   -2   870  -871                      $ Clad

1182  3   0.10018       1   -2    11   -12    76   -77   871    $ Water

1183  1   0.068525      1   -2  -872                            $ Fuel

1184  2   0.055323      1   -2   872  -873                      $ Clad

1185  3   0.10018       1   -2    11   -12    77   -78   873    $ Water

1186  1   0.068525      1   -2  -874                            $ Fuel

1187  2   0.055323      1   -2   874  -875                      $ Clad

1188  3   0.10018       1   -2    11   -12    78   -79   875    $ Water

1189  1   0.068525      1   -2  -876                            $ Fuel

1190  2   0.055323      1   -2   876  -877                      $ Clad

1191  3   0.10018       1   -2    11   -12    79   -80   877    $ Water

1192  1   0.068525      1   -2  -878                            $ Fuel

1193  2   0.055323      1   -2   878  -879                      $ Clad

1194  3   0.10018       1   -2    11   -12    80   -81   879    $ Water

1195  1   0.068525      1   -2  -880                            $ Fuel

1196  2   0.055323      1   -2   880  -881                      $ Clad

1197  3   0.10018       1   -2    11   -12    81   -82   881    $ Water

1198  1   0.068525      1   -2  -882                            $ Fuel

1199  2   0.055323      1   -2   882  -883                      $ Clad

1200  3   0.10018       1   -2    11   -12    82   -83   883    $ Water

1201  1   0.068525      1   -2  -884                            $ Fuel

1202  2   0.055323      1   -2   884  -885                      $ Clad

1203  3   0.10018       1   -2    11   -12    83   -84   885    $ Water

1204  1   0.068525      1   -2  -886                            $ Fuel

1205  2   0.055323      1   -2   886  -887                      $ Clad

1206  3   0.10018       1   -2    11   -12    84   -85   887    $ Water

1207  1   0.068525      1   -2  -888                            $ Fuel

1208  2   0.055323      1   -2   888  -889                      $ Clad

1209  3   0.10018       1   -2    11   -12    85   -86   889    $ Water

1210  1   0.068525      1   -2  -890                            $ Fuel

1211  2   0.055323      1   -2   890  -891                      $ Clad

1212  3   0.10018       1   -2    11   -12    86   -87   891    $ Water

1213  3   0.10018       1   -2    11   -12    87    -5          $ Reflector

1214  1   0.068525      1   -2  -892                            $ Fuel

1215  2   0.055323      1   -2   892  -893                      $ Clad

1216  3   0.10018       1   -2    12   -13    69   -70   893    $ Water

1217  1   0.068525      1   -2  -894                            $ Fuel

1218  2   0.055323      1   -2   894  -895                      $ Clad

1219  3   0.10018       1   -2    12   -13    70   -71   895    $ Water

1220  1   0.068525      1   -2  -896                            $ Fuel

1221  2   0.055323      1   -2   896  -897                      $ Clad

1222  3   0.10018       1   -2    12   -13    71   -72   897    $ Water

1223  1   0.068525      1   -2  -898                            $ Fuel

1224  2   0.055323      1   -2   898  -899                      $ Clad

1225  3   0.10018       1   -2    12   -13    72   -73   899    $ Water

1226  1   0.068525      1   -2  -900                            $ Fuel

1227  2   0.055323      1   -2   900  -901                      $ Clad

1228  3   0.10018       1   -2    12   -13    73   -74   901    $ Water

1229  1   0.068525      1   -2  -902                            $ Fuel

1230  2   0.055323      1   -2   902  -903                      $ Clad

1231  3   0.10018       1   -2    12   -13    74   -75   903    $ Water

1232  1   0.068525      1   -2  -904                            $ Fuel

1233  2   0.055323      1   -2   904  -905                      $ Clad

1234  3   0.10018       1   -2    12   -13    75   -76   905    $ Water

1235  1   0.068525      1   -2  -906                            $ Fuel

1236  2   0.055323      1   -2   906  -907                      $ Clad

1237  3   0.10018       1   -2    12   -13    76   -77   907    $ Water

1238  1   0.068525      1   -2  -908                            $ Fuel

1239  2   0.055323      1   -2   908  -909                      $ Clad

1240  3   0.10018       1   -2    12   -13    77   -78   909    $ Water

1241  1   0.068525      1   -2  -910                            $ Fuel

1242  2   0.055323      1   -2   910  -911                      $ Clad

1243  3   0.10018       1   -2    12   -13    78   -79   911    $ Water

1244  1   0.068525      1   -2  -912                            $ Fuel

1245  2   0.055323      1   -2   912  -913                      $ Clad

1246  3   0.10018       1   -2    12   -13    79   -80   913    $ Water

1247  1   0.068525      1   -2  -914                            $ Fuel

1248  2   0.055323      1   -2   914  -915                      $ Clad

1249  3   0.10018       1   -2    12   -13    80   -81   915    $ Water

1250  1   0.068525      1   -2  -916                            $ Fuel

1251  2   0.055323      1   -2   916  -917                      $ Clad

1252  3   0.10018       1   -2    12   -13    81   -82   917    $ Water

1253  1   0.068525      1   -2  -918                            $ Fuel

1254  2   0.055323      1   -2   918  -919                      $ Clad

1255  3   0.10018       1   -2    12   -13    82   -83   919    $ Water

1256  1   0.068525      1   -2  -920                            $ Fuel

1257  2   0.055323      1   -2   920  -921                      $ Clad

1258  3   0.10018       1   -2    12   -13    83   -84   921    $ Water

1259  1   0.068525      1   -2  -922                            $ Fuel

1260  2   0.055323      1   -2   922  -923                      $ Clad

1261  3   0.10018       1   -2    12   -13    84   -85   923    $ Water

1262  1   0.068525      1   -2  -924                            $ Fuel

1263  2   0.055323      1   -2   924  -925                      $ Clad

1264  3   0.10018       1   -2    12   -13    85   -86   925    $ Water

1265  1   0.068525      1   -2  -926                            $ Fuel

1266  2   0.055323      1   -2   926  -927                      $ Clad

1267  3   0.10018       1   -2    12   -13    86   -87   927    $ Water

1268  3   0.10018       1   -2    12   -13    87    -5          $ Reflector

1269  1   0.068525      1   -2  -928                            $ Fuel

1270  2   0.055323      1   -2   928  -929                      $ Clad

1271  3   0.10018       1   -2    13   -14    69   -70   929    $ Water

1272  1   0.068525      1   -2  -930                            $ Fuel

1273  2   0.055323      1   -2   930  -931                      $ Clad

1274  3   0.10018       1   -2    13   -14    70   -71   931    $ Water

1275  1   0.068525      1   -2  -932                            $ Fuel

1276  2   0.055323      1   -2   932  -933                      $ Clad

1277  3   0.10018       1   -2    13   -14    71   -72   933    $ Water

1278  1   0.068525      1   -2  -934                            $ Fuel

1279  2   0.055323      1   -2   934  -935                      $ Clad

1280  3   0.10018       1   -2    13   -14    72   -73   935    $ Water

1281  1   0.068525      1   -2  -936                            $ Fuel

1282  2   0.055323      1   -2   936  -937                      $ Clad

1283  3   0.10018       1   -2    13   -14    73   -74   937    $ Water

1284  1   0.068525      1   -2  -938                            $ Fuel

1285  2   0.055323      1   -2   938  -939                      $ Clad

1286  3   0.10018       1   -2    13   -14    74   -75   939    $ Water

1287  1   0.068525      1   -2  -940                            $ Fuel

1288  2   0.055323      1   -2   940  -941                      $ Clad

1289  3   0.10018       1   -2    13   -14    75   -76   941    $ Water

1290  1   0.068525      1   -2  -942                            $ Fuel

1291  2   0.055323      1   -2   942  -943                      $ Clad

1292  3   0.10018       1   -2    13   -14    76   -77   943    $ Water

1293  1   0.068525      1   -2  -944                            $ Fuel

1294  2   0.055323      1   -2   944  -945                      $ Clad

1295  3   0.10018       1   -2    13   -14    77   -78   945    $ Water

1296  1   0.068525      1   -2  -946                            $ Fuel

1297  2   0.055323      1   -2   946  -947                      $ Clad

1298  3   0.10018       1   -2    13   -14    78   -79   947    $ Water

1299  1   0.068525      1   -2  -948                            $ Fuel

1300  2   0.055323      1   -2   948  -949                      $ Clad

1301  3   0.10018       1   -2    13   -14    79   -80   949    $ Water

1302  1   0.068525      1   -2  -950                            $ Fuel

1303  2   0.055323      1   -2   950  -951                      $ Clad

1304  3   0.10018       1   -2    13   -14    80   -81   951    $ Water

1305  1   0.068525      1   -2  -952                            $ Fuel

1306  2   0.055323      1   -2   952  -953                      $ Clad

1307  3   0.10018       1   -2    13   -14    81   -82   953    $ Water

1308  1   0.068525      1   -2  -954                            $ Fuel

1309  2   0.055323      1   -2   954  -955                      $ Clad

1310  3   0.10018       1   -2    13   -14    82   -83   955    $ Water

1311  1   0.068525      1   -2  -956                            $ Fuel

1312  2   0.055323      1   -2   956  -957                      $ Clad

1313  3   0.10018       1   -2    13   -14    83   -84   957    $ Water

1314  1   0.068525      1   -2  -958                            $ Fuel

1315  2   0.055323      1   -2   958  -959                      $ Clad

1316  3   0.10018       1   -2    13   -14    84   -85   959    $ Water

1317  1   0.068525      1   -2  -960                            $ Fuel

1318  2   0.055323      1   -2   960  -961                      $ Clad

1319  3   0.10018       1   -2    13   -14    85   -86   961    $ Water

1320  1   0.068525      1   -2  -962                            $ Fuel

1321  2   0.055323      1   -2   962  -963                      $ Clad

1322  3   0.10018       1   -2    13   -14    86   -87   963    $ Water

1323  3   0.10018       1   -2    13   -14    87    -5          $ Reflector

1324  1   0.068525      1   -2  -964                            $ Fuel

1325  2   0.055323      1   -2   964  -965                      $ Clad

1326  3   0.10018       1   -2    14   -15    69   -70   965    $ Water

1327  1   0.068525      1   -2  -966                            $ Fuel

1328  2   0.055323      1   -2   966  -967                      $ Clad

1329  3   0.10018       1   -2    14   -15    70   -71   967    $ Water

1330  1   0.068525      1   -2  -968                            $ Fuel

1331  2   0.055323      1   -2   968  -969                      $ Clad

1332  3   0.10018       1   -2    14   -15    71   -72   969    $ Water

1333  1   0.068525      1   -2  -970                            $ Fuel

1334  2   0.055323      1   -2   970  -971                      $ Clad

1335  3   0.10018       1   -2    14   -15    72   -73   971    $ Water

1336  1   0.068525      1   -2  -972                            $ Fuel

1337  2   0.055323      1   -2   972  -973                      $ Clad

1338  3   0.10018       1   -2    14   -15    73   -74   973    $ Water

1339  1   0.068525      1   -2  -974                            $ Fuel

1340  2   0.055323      1   -2   974  -975                      $ Clad

1341  3   0.10018       1   -2    14   -15    74   -75   975    $ Water

1342  1   0.068525      1   -2  -976                            $ Fuel

1343  2   0.055323      1   -2   976  -977                      $ Clad

1344  3   0.10018       1   -2    14   -15    75   -76   977    $ Water

1345  1   0.068525      1   -2  -978                            $ Fuel

1346  2   0.055323      1   -2   978  -979                      $ Clad

1347  3   0.10018       1   -2    14   -15    76   -77   979    $ Water

1348  1   0.068525      1   -2  -980                            $ Fuel

1349  2   0.055323      1   -2   980  -981                      $ Clad

1350  3   0.10018       1   -2    14   -15    77   -78   981    $ Water

1351  1   0.068525      1   -2  -982                            $ Fuel

1352  2   0.055323      1   -2   982  -983                      $ Clad

1353  3   0.10018       1   -2    14   -15    78   -79   983    $ Water

1354  1   0.068525      1   -2  -984                            $ Fuel

1355  2   0.055323      1   -2   984  -985                      $ Clad

1356  3   0.10018       1   -2    14   -15    79   -80   985    $ Water

1357  1   0.068525      1   -2  -986                            $ Fuel

1358  2   0.055323      1   -2   986  -987                      $ Clad

1359  3   0.10018       1   -2    14   -15    80   -81   987    $ Water

1360  1   0.068525      1   -2  -988                            $ Fuel

1361  2   0.055323      1   -2   988  -989                      $ Clad

1362  3   0.10018       1   -2    14   -15    81   -82   989    $ Water

1363  1   0.068525      1   -2  -990                            $ Fuel

1364  2   0.055323      1   -2   990  -991                      $ Clad

1365  3   0.10018       1   -2    14   -15    82   -83   991    $ Water

1366  1   0.068525      1   -2  -992                            $ Fuel

1367  2   0.055323      1   -2   992  -993                      $ Clad

1368  3   0.10018       1   -2    14   -15    83   -84   993    $ Water

1369  1   0.068525      1   -2  -994                            $ Fuel

1370  2   0.055323      1   -2   994  -995                      $ Clad

1371  3   0.10018       1   -2    14   -15    84   -85   995    $ Water

1372  1   0.068525      1   -2  -996                            $ Fuel

1373  2   0.055323      1   -2   996  -997                      $ Clad

1374  3   0.10018       1   -2    14   -15    85   -86   997    $ Water

1375  1   0.068525      1   -2  -998                            $ Fuel

1376  2   0.055323      1   -2   998  -999                      $ Clad

1377  3   0.10018       1   -2    14   -15    86   -87   999    $ Water

1378  3   0.10018       1   -2    14   -15    87    -5          $ Reflector

1379  1   0.068525      1   -2 -1000                            $ Fuel

1380  2   0.055323      1   -2  1000 -1001                      $ Clad

1381  3   0.10018       1   -2    15   -16    69   -70  1001    $ Water

1382  1   0.068525      1   -2 -1002                            $ Fuel

1383  2   0.055323      1   -2  1002 -1003                      $ Clad

1384  3   0.10018       1   -2    15   -16    70   -71  1003    $ Water

1385  1   0.068525      1   -2 -1004                            $ Fuel

1386  2   0.055323      1   -2  1004 -1005                      $ Clad

1387  3   0.10018       1   -2    15   -16    71   -72  1005    $ Water

1388  1   0.068525      1   -2 -1006                            $ Fuel

1389  2   0.055323      1   -2  1006 -1007                      $ Clad

1390  3   0.10018       1   -2    15   -16    72   -73  1007    $ Water

1391  1   0.068525      1   -2 -1008                            $ Fuel

1392  2   0.055323      1   -2  1008 -1009                      $ Clad

1393  3   0.10018       1   -2    15   -16    73   -74  1009    $ Water

1394  1   0.068525      1   -2 -1010                            $ Fuel

1395  2   0.055323      1   -2  1010 -1011                      $ Clad

1396  3   0.10018       1   -2    15   -16    74   -75  1011    $ Water

1397  1   0.068525      1   -2 -1012                            $ Fuel

1398  2   0.055323      1   -2  1012 -1013                      $ Clad

1399  3   0.10018       1   -2    15   -16    75   -76  1013    $ Water

1400  1   0.068525      1   -2 -1014                            $ Fuel

1401  2   0.055323      1   -2  1014 -1015                      $ Clad

1402  3   0.10018       1   -2    15   -16    76   -77  1015    $ Water

1403  1   0.068525      1   -2 -1016                            $ Fuel

1404  2   0.055323      1   -2  1016 -1017                      $ Clad

1405  3   0.10018       1   -2    15   -16    77   -78  1017    $ Water

1406  1   0.068525      1   -2 -1018                            $ Fuel

1407  2   0.055323      1   -2  1018 -1019                      $ Clad

1408  3   0.10018       1   -2    15   -16    78   -79  1019    $ Water

1409  1   0.068525      1   -2 -1020                            $ Fuel

1410  2   0.055323      1   -2  1020 -1021                      $ Clad

1411  3   0.10018       1   -2    15   -16    79   -80  1021    $ Water

1412  1   0.068525      1   -2 -1022                            $ Fuel

1413  2   0.055323      1   -2  1022 -1023                      $ Clad

1414  3   0.10018       1   -2    15   -16    80   -81  1023    $ Water

1415  1   0.068525      1   -2 -1024                            $ Fuel

1416  2   0.055323      1   -2  1024 -1025                      $ Clad

1417  3   0.10018       1   -2    15   -16    81   -82  1025    $ Water

1418  1   0.068525      1   -2 -1026                            $ Fuel

1419  2   0.055323      1   -2  1026 -1027                      $ Clad

1420  3   0.10018       1   -2    15   -16    82   -83  1027    $ Water

1421  1   0.068525      1   -2 -1028                            $ Fuel

1422  2   0.055323      1   -2  1028 -1029                      $ Clad

1423  3   0.10018       1   -2    15   -16    83   -84  1029    $ Water

1424  1   0.068525      1   -2 -1030                            $ Fuel

1425  2   0.055323      1   -2  1030 -1031                      $ Clad

1426  3   0.10018       1   -2    15   -16    84   -85  1031    $ Water

1427  1   0.068525      1   -2 -1032                            $ Fuel

1428  2   0.055323      1   -2  1032 -1033                      $ Clad

1429  3   0.10018       1   -2    15   -16    85   -86  1033    $ Water

1430  1   0.068525      1   -2 -1034                            $ Fuel

1431  2   0.055323      1   -2  1034 -1035                      $ Clad

1432  3   0.10018       1   -2    15   -16    86   -87  1035    $ Water

1433  3   0.10018       1   -2    15   -16    87    -5          $ Reflector

1434  1   0.068525      1   -2 -1036                            $ Fuel

1435  2   0.055323      1   -2  1036 -1037                      $ Clad

1436  3   0.10018       1   -2    16   -17    69   -70  1037    $ Water

1437  1   0.068525      1   -2 -1038                            $ Fuel

1438  2   0.055323      1   -2  1038 -1039                      $ Clad

1439  3   0.10018       1   -2    16   -17    70   -71  1039    $ Water

1440  1   0.068525      1   -2 -1040                            $ Fuel

1441  2   0.055323      1   -2  1040 -1041                      $ Clad

1442  3   0.10018       1   -2    16   -17    71   -72  1041    $ Water

1443  1   0.068525      1   -2 -1042                            $ Fuel

1444  2   0.055323      1   -2  1042 -1043                      $ Clad

1445  3   0.10018       1   -2    16   -17    72   -73  1043    $ Water

1446  1   0.068525      1   -2 -1044                            $ Fuel

1447  2   0.055323      1   -2  1044 -1045                      $ Clad

1448  3   0.10018       1   -2    16   -17    73   -74  1045    $ Water

1449  1   0.068525      1   -2 -1046                            $ Fuel

1450  2   0.055323      1   -2  1046 -1047                      $ Clad

1451  3   0.10018       1   -2    16   -17    74   -75  1047    $ Water

1452  1   0.068525      1   -2 -1048                            $ Fuel

1453  2   0.055323      1   -2  1048 -1049                      $ Clad

1454  3   0.10018       1   -2    16   -17    75   -76  1049    $ Water

1455  1   0.068525      1   -2 -1050                            $ Fuel

1456  2   0.055323      1   -2  1050 -1051                      $ Clad

1457  3   0.10018       1   -2    16   -17    76   -77  1051    $ Water

1458  1   0.068525      1   -2 -1052                            $ Fuel

1459  2   0.055323      1   -2  1052 -1053                      $ Clad

1460  3   0.10018       1   -2    16   -17    77   -78  1053    $ Water

1461  1   0.068525      1   -2 -1054                            $ Fuel

1462  2   0.055323      1   -2  1054 -1055                      $ Clad

1463  3   0.10018       1   -2    16   -17    78   -79  1055    $ Water

1464  1   0.068525      1   -2 -1056                            $ Fuel

1465  2   0.055323      1   -2  1056 -1057                      $ Clad

1466  3   0.10018       1   -2    16   -17    79   -80  1057    $ Water

1467  1   0.068525      1   -2 -1058                            $ Fuel

1468  2   0.055323      1   -2  1058 -1059                      $ Clad

1469  3   0.10018       1   -2    16   -17    80   -81  1059    $ Water

1470  1   0.068525      1   -2 -1060                            $ Fuel

1471  2   0.055323      1   -2  1060 -1061                      $ Clad

1472  3   0.10018       1   -2    16   -17    81   -82  1061    $ Water

1473  3   0.10018       1   -2    16   -17    82    -5          $ Reflector

1474  1   0.068525      1   -2 -1062                            $ Fuel

1475  2   0.055323      1   -2  1062 -1063                      $ Clad

1476  3   0.10018       1   -2    17   -18    69   -70  1063    $ Water

1477  1   0.068525      1   -2 -1064                            $ Fuel

1478  2   0.055323      1   -2  1064 -1065                      $ Clad

1479  3   0.10018       1   -2    17   -18    70   -71  1065    $ Water

1480  1   0.068525      1   -2 -1066                            $ Fuel

1481  2   0.055323      1   -2  1066 -1067                      $ Clad

1482  3   0.10018       1   -2    17   -18    71   -72  1067    $ Water

1483  1   0.068525      1   -2 -1068                            $ Fuel

1484  2   0.055323      1   -2  1068 -1069                      $ Clad

1485  3   0.10018       1   -2    17   -18    72   -73  1069    $ Water

1486  1   0.068525      1   -2 -1070                            $ Fuel

1487  2   0.055323      1   -2  1070 -1071                      $ Clad

1488  3   0.10018       1   -2    17   -18    73   -74  1071    $ Water

1489  1   0.068525      1   -2 -1072                            $ Fuel

1490  2   0.055323      1   -2  1072 -1073                      $ Clad

1491  3   0.10018       1   -2    17   -18    74   -75  1073    $ Water

1492  1   0.068525      1   -2 -1074                            $ Fuel

1493  2   0.055323      1   -2  1074 -1075                      $ Clad

1494  3   0.10018       1   -2    17   -18    75   -76  1075    $ Water

1495  1   0.068525      1   -2 -1076                            $ Fuel

1496  2   0.055323      1   -2  1076 -1077                      $ Clad

1497  3   0.10018       1   -2    17   -18    76   -77  1077    $ Water

1498  1   0.068525      1   -2 -1078                            $ Fuel

1499  2   0.055323      1   -2  1078 -1079                      $ Clad

1500  3   0.10018       1   -2    17   -18    77   -78  1079    $ Water

1501  1   0.068525      1   -2 -1080                            $ Fuel

1502  2   0.055323      1   -2  1080 -1081                      $ Clad

1503  3   0.10018       1   -2    17   -18    78   -79  1081    $ Water

1504  1   0.068525      1   -2 -1082                            $ Fuel

1505  2   0.055323      1   -2  1082 -1083                      $ Clad

1506  3   0.10018       1   -2    17   -18    79   -80  1083    $ Water

1507  1   0.068525      1   -2 -1084                            $ Fuel

1508  2   0.055323      1   -2  1084 -1085                      $ Clad

1509  3   0.10018       1   -2    17   -18    80   -81  1085    $ Water

1510  1   0.068525      1   -2 -1086                            $ Fuel

1511  2   0.055323      1   -2  1086 -1087                      $ Clad

1512  3   0.10018       1   -2    17   -18    81   -82  1087    $ Water

1513  3   0.10018       1   -2    17   -18    82    -5          $ Reflector

1514  1   0.068525      1   -2 -1088                            $ Fuel

1515  2   0.055323      1   -2  1088 -1089                      $ Clad

1516  3   0.10018       1   -2    18   -19    69   -70  1089    $ Water

1517  1   0.068525      1   -2 -1090                            $ Fuel

1518  2   0.055323      1   -2  1090 -1091                      $ Clad

1519  3   0.10018       1   -2    18   -19    70   -71  1091    $ Water

1520  1   0.068525      1   -2 -1092                            $ Fuel

1521  2   0.055323      1   -2  1092 -1093                      $ Clad

1522  3   0.10018       1   -2    18   -19    71   -72  1093    $ Water

1523  1   0.068525      1   -2 -1094                            $ Fuel

1524  2   0.055323      1   -2  1094 -1095                      $ Clad

1525  3   0.10018       1   -2    18   -19    72   -73  1095    $ Water

1526  1   0.068525      1   -2 -1096                            $ Fuel

1527  2   0.055323      1   -2  1096 -1097                      $ Clad

1528  3   0.10018       1   -2    18   -19    73   -74  1097    $ Water

1529  1   0.068525      1   -2 -1098                            $ Fuel

1530  2   0.055323      1   -2  1098 -1099                      $ Clad

1531  3   0.10018       1   -2    18   -19    74   -75  1099    $ Water

1532  1   0.068525      1   -2 -1100                            $ Fuel

1533  2   0.055323      1   -2  1100 -1101                      $ Clad

1534  3   0.10018       1   -2    18   -19    75   -76  1101    $ Water

1535  1   0.068525      1   -2 -1102                            $ Fuel

1536  2   0.055323      1   -2  1102 -1103                      $ Clad

1537  3   0.10018       1   -2    18   -19    76   -77  1103    $ Water

1538  1   0.068525      1   -2 -1104                            $ Fuel

1539  2   0.055323      1   -2  1104 -1105                      $ Clad

1540  3   0.10018       1   -2    18   -19    77   -78  1105    $ Water

1541  1   0.068525      1   -2 -1106                            $ Fuel

1542  2   0.055323      1   -2  1106 -1107                      $ Clad

1543  3   0.10018       1   -2    18   -19    78   -79  1107    $ Water

1544  1   0.068525      1   -2 -1108                            $ Fuel

1545  2   0.055323      1   -2  1108 -1109                      $ Clad

1546  3   0.10018       1   -2    18   -19    79   -80  1109    $ Water

1547  1   0.068525      1   -2 -1110                            $ Fuel

1548  2   0.055323      1   -2  1110 -1111                      $ Clad

1549  3   0.10018       1   -2    18   -19    80   -81  1111    $ Water

1550  1   0.068525      1   -2 -1112                            $ Fuel

1551  2   0.055323      1   -2  1112 -1113                      $ Clad

1552  3   0.10018       1   -2    18   -19    81   -82  1113    $ Water

1553  3   0.10018       1   -2    18   -19    82    -5          $ Reflector

1554  1   0.068525      1   -2 -1114                            $ Fuel

1555  2   0.055323      1   -2  1114 -1115                      $ Clad

1556  3   0.10018       1   -2    19   -20    69   -70  1115    $ Water

1557  1   0.068525      1   -2 -1116                            $ Fuel

1558  2   0.055323      1   -2  1116 -1117                      $ Clad

1559  3   0.10018       1   -2    19   -20    70   -71  1117    $ Water

1560  1   0.068525      1   -2 -1118                            $ Fuel

1561  2   0.055323      1   -2  1118 -1119                      $ Clad

1562  3   0.10018       1   -2    19   -20    71   -72  1119    $ Water

1563  1   0.068525      1   -2 -1120                            $ Fuel

1564  2   0.055323      1   -2  1120 -1121                      $ Clad

1565  3   0.10018       1   -2    19   -20    72   -73  1121    $ Water

1566  1   0.068525      1   -2 -1122                            $ Fuel

1567  2   0.055323      1   -2  1122 -1123                      $ Clad

1568  3   0.10018       1   -2    19   -20    73   -74  1123    $ Water

1569  1   0.068525      1   -2 -1124                            $ Fuel

1570  2   0.055323      1   -2  1124 -1125                      $ Clad

1571  3   0.10018       1   -2    19   -20    74   -75  1125    $ Water

1572  1   0.068525      1   -2 -1126                            $ Fuel

1573  2   0.055323      1   -2  1126 -1127                      $ Clad

1574  3   0.10018       1   -2    19   -20    75   -76  1127    $ Water

1575  1   0.068525      1   -2 -1128                            $ Fuel

1576  2   0.055323      1   -2  1128 -1129                      $ Clad

1577  3   0.10018       1   -2    19   -20    76   -77  1129    $ Water

1578  1   0.068525      1   -2 -1130                            $ Fuel

1579  2   0.055323      1   -2  1130 -1131                      $ Clad

1580  3   0.10018       1   -2    19   -20    77   -78  1131    $ Water

1581  1   0.068525      1   -2 -1132                            $ Fuel

1582  2   0.055323      1   -2  1132 -1133                      $ Clad

1583  3   0.10018       1   -2    19   -20    78   -79  1133    $ Water

1584  1   0.068525      1   -2 -1134                            $ Fuel

1585  2   0.055323      1   -2  1134 -1135                      $ Clad

1586  3   0.10018       1   -2    19   -20    79   -80  1135    $ Water

1587  1   0.068525      1   -2 -1136                            $ Fuel

1588  2   0.055323      1   -2  1136 -1137                      $ Clad

1589  3   0.10018       1   -2    19   -20    80   -81  1137    $ Water

1590  1   0.068525      1   -2 -1138                            $ Fuel

1591  2   0.055323      1   -2  1138 -1139                      $ Clad

1592  3   0.10018       1   -2    19   -20    81   -82  1139    $ Water

1593  3   0.10018       1   -2    19   -20    82    -5          $ Reflector

1594  1   0.068525      1   -2 -1140                            $ Fuel

1595  2   0.055323      1   -2  1140 -1141                      $ Clad

1596  3   0.10018       1   -2    20   -21    69   -70  1141    $ Water

1597  1   0.068525      1   -2 -1142                            $ Fuel

1598  2   0.055323      1   -2  1142 -1143                      $ Clad

1599  3   0.10018       1   -2    20   -21    70   -71  1143    $ Water

1600  1   0.068525      1   -2 -1144                            $ Fuel

1601  2   0.055323      1   -2  1144 -1145                      $ Clad

1602  3   0.10018       1   -2    20   -21    71   -72  1145    $ Water

1603  1   0.068525      1   -2 -1146                            $ Fuel

1604  2   0.055323      1   -2  1146 -1147                      $ Clad

1605  3   0.10018       1   -2    20   -21    72   -73  1147    $ Water

1606  1   0.068525      1   -2 -1148                            $ Fuel

1607  2   0.055323      1   -2  1148 -1149                      $ Clad

1608  3   0.10018       1   -2    20   -21    73   -74  1149    $ Water

1609  1   0.068525      1   -2 -1150                            $ Fuel

1610  2   0.055323      1   -2  1150 -1151                      $ Clad

1611  3   0.10018       1   -2    20   -21    74   -75  1151    $ Water

1612  1   0.068525      1   -2 -1152                            $ Fuel

1613  2   0.055323      1   -2  1152 -1153                      $ Clad

1614  3   0.10018       1   -2    20   -21    75   -76  1153    $ Water

1615  1   0.068525      1   -2 -1154                            $ Fuel

1616  2   0.055323      1   -2  1154 -1155                      $ Clad

1617  3   0.10018       1   -2    20   -21    76   -77  1155    $ Water

1618  1   0.068525      1   -2 -1156                            $ Fuel

1619  2   0.055323      1   -2  1156 -1157                      $ Clad

1620  3   0.10018       1   -2    20   -21    77   -78  1157    $ Water

1621  1   0.068525      1   -2 -1158                            $ Fuel

1622  2   0.055323      1   -2  1158 -1159                      $ Clad

1623  3   0.10018       1   -2    20   -21    78   -79  1159    $ Water

1624  1   0.068525      1   -2 -1160                            $ Fuel

1625  2   0.055323      1   -2  1160 -1161                      $ Clad

1626  3   0.10018       1   -2    20   -21    79   -80  1161    $ Water

1627  1   0.068525      1   -2 -1162                            $ Fuel

1628  2   0.055323      1   -2  1162 -1163                      $ Clad

1629  3   0.10018       1   -2    20   -21    80   -81  1163    $ Water

1630  1   0.068525      1   -2 -1164                            $ Fuel

1631  2   0.055323      1   -2  1164 -1165                      $ Clad

1632  3   0.10018       1   -2    20   -21    81   -82  1165    $ Water

1633  3   0.10018       1   -2    20   -21    82    -5          $ Reflector

1634  1   0.068525      1   -2 -1166                            $ Fuel

1635  2   0.055323      1   -2  1166 -1167                      $ Clad

1636  3   0.10018       1   -2    21   -22    69   -70  1167    $ Water

1637  1   0.068525      1   -2 -1168                            $ Fuel

1638  2   0.055323      1   -2  1168 -1169                      $ Clad

1639  3   0.10018       1   -2    21   -22    70   -71  1169    $ Water

1640  1   0.068525      1   -2 -1170                            $ Fuel

1641  2   0.055323      1   -2  1170 -1171                      $ Clad

1642  3   0.10018       1   -2    21   -22    71   -72  1171    $ Water

1643  1   0.068525      1   -2 -1172                            $ Fuel

1644  2   0.055323      1   -2  1172 -1173                      $ Clad

1645  3   0.10018       1   -2    21   -22    72   -73  1173    $ Water

1646  1   0.068525      1   -2 -1174                            $ Fuel

1647  2   0.055323      1   -2  1174 -1175                      $ Clad

1648  3   0.10018       1   -2    21   -22    73   -74  1175    $ Water

1649  1   0.068525      1   -2 -1176                            $ Fuel

1650  2   0.055323      1   -2  1176 -1177                      $ Clad

1651  3   0.10018       1   -2    21   -22    74   -75  1177    $ Water

1652  1   0.068525      1   -2 -1178                            $ Fuel

1653  2   0.055323      1   -2  1178 -1179                      $ Clad

1654  3   0.10018       1   -2    21   -22    75   -76  1179    $ Water

1655  1   0.068525      1   -2 -1180                            $ Fuel

1656  2   0.055323      1   -2  1180 -1181                      $ Clad

1657  3   0.10018       1   -2    21   -22    76   -77  1181    $ Water

1658  1   0.068525      1   -2 -1182                            $ Fuel

1659  2   0.055323      1   -2  1182 -1183                      $ Clad

1660  3   0.10018       1   -2    21   -22    77   -78  1183    $ Water

1661  1   0.068525      1   -2 -1184                            $ Fuel

1662  2   0.055323      1   -2  1184 -1185                      $ Clad

1663  3   0.10018       1   -2    21   -22    78   -79  1185    $ Water

1664  1   0.068525      1   -2 -1186                            $ Fuel

1665  2   0.055323      1   -2  1186 -1187                      $ Clad

1666  3   0.10018       1   -2    21   -22    79   -80  1187    $ Water

1667  1   0.068525      1   -2 -1188                            $ Fuel

1668  2   0.055323      1   -2  1188 -1189                      $ Clad

1669  3   0.10018       1   -2    21   -22    80   -81  1189    $ Water

1670  1   0.068525      1   -2 -1190                            $ Fuel

1671  2   0.055323      1   -2  1190 -1191                      $ Clad

1672  3   0.10018       1   -2    21   -22    81   -82  1191    $ Water

1673  3   0.10018       1   -2    21   -22    82    -5          $ Reflector

1674  1   0.068525      1   -2 -1192                            $ Fuel

1675  2   0.055323      1   -2  1192 -1193                      $ Clad

1676  3   0.10018       1   -2    22   -23    69   -70  1193    $ Water

1677  1   0.068525      1   -2 -1194                            $ Fuel

1678  2   0.055323      1   -2  1194 -1195                      $ Clad

1679  3   0.10018       1   -2    22   -23    70   -71  1195    $ Water

1680  1   0.068525      1   -2 -1196                            $ Fuel

1681  2   0.055323      1   -2  1196 -1197                      $ Clad

1682  3   0.10018       1   -2    22   -23    71   -72  1197    $ Water

1683  1   0.068525      1   -2 -1198                            $ Fuel

1684  2   0.055323      1   -2  1198 -1199                      $ Clad

1685  3   0.10018       1   -2    22   -23    72   -73  1199    $ Water

1686  1   0.068525      1   -2 -1200                            $ Fuel

1687  2   0.055323      1   -2  1200 -1201                      $ Clad

1688  3   0.10018       1   -2    22   -23    73   -74  1201    $ Water

1689  1   0.068525      1   -2 -1202                            $ Fuel

1690  2   0.055323      1   -2  1202 -1203                      $ Clad

1691  3   0.10018       1   -2    22   -23    74   -75  1203    $ Water

1692  1   0.068525      1   -2 -1204                            $ Fuel

1693  2   0.055323      1   -2  1204 -1205                      $ Clad

1694  3   0.10018       1   -2    22   -23    75   -76  1205    $ Water

1695  1   0.068525      1   -2 -1206                            $ Fuel

1696  2   0.055323      1   -2  1206 -1207                      $ Clad

1697  3   0.10018       1   -2    22   -23    76   -77  1207    $ Water

1698  1   0.068525      1   -2 -1208                            $ Fuel

1699  2   0.055323      1   -2  1208 -1209                      $ Clad

1700  3   0.10018       1   -2    22   -23    77   -78  1209    $ Water

1701  1   0.068525      1   -2 -1210                            $ Fuel

1702  2   0.055323      1   -2  1210 -1211                      $ Clad

1703  3   0.10018       1   -2    22   -23    78   -79  1211    $ Water

1704  1   0.068525      1   -2 -1212                            $ Fuel

1705  2   0.055323      1   -2  1212 -1213                      $ Clad

1706  3   0.10018       1   -2    22   -23    79   -80  1213    $ Water

1707  1   0.068525      1   -2 -1214                            $ Fuel

1708  2   0.055323      1   -2  1214 -1215                      $ Clad

1709  3   0.10018       1   -2    22   -23    80   -81  1215    $ Water

1710  1   0.068525      1   -2 -1216                            $ Fuel

1711  2   0.055323      1   -2  1216 -1217                      $ Clad

1712  3   0.10018       1   -2    22   -23    81   -82  1217    $ Water

1713  3   0.10018       1   -2    22   -23    82    -5          $ Reflector

1714  1   0.068525      1   -2 -1218                            $ Fuel

1715  2   0.055323      1   -2  1218 -1219                      $ Clad

1716  3   0.10018       1   -2    23   -24    69   -70  1219    $ Water

1717  1   0.068525      1   -2 -1220                            $ Fuel

1718  2   0.055323      1   -2  1220 -1221                      $ Clad

1719  3   0.10018       1   -2    23   -24    70   -71  1221    $ Water

1720  1   0.068525      1   -2 -1222                            $ Fuel

1721  2   0.055323      1   -2  1222 -1223                      $ Clad

1722  3   0.10018       1   -2    23   -24    71   -72  1223    $ Water

1723  1   0.068525      1   -2 -1224                            $ Fuel

1724  2   0.055323      1   -2  1224 -1225                      $ Clad

1725  3   0.10018       1   -2    23   -24    72   -73  1225    $ Water

1726  1   0.068525      1   -2 -1226                            $ Fuel

1727  2   0.055323      1   -2  1226 -1227                      $ Clad

1728  3   0.10018       1   -2    23   -24    73   -74  1227    $ Water

1729  1   0.068525      1   -2 -1228                            $ Fuel

1730  2   0.055323      1   -2  1228 -1229                      $ Clad

1731  3   0.10018       1   -2    23   -24    74   -75  1229    $ Water

1732  1   0.068525      1   -2 -1230                            $ Fuel

1733  2   0.055323      1   -2  1230 -1231                      $ Clad

1734  3   0.10018       1   -2    23   -24    75   -76  1231    $ Water

1735  1   0.068525      1   -2 -1232                            $ Fuel

1736  2   0.055323      1   -2  1232 -1233                      $ Clad

1737  3   0.10018       1   -2    23   -24    76   -77  1233    $ Water

1738  1   0.068525      1   -2 -1234                            $ Fuel

1739  2   0.055323      1   -2  1234 -1235                      $ Clad

1740  3   0.10018       1   -2    23   -24    77   -78  1235    $ Water

1741  1   0.068525      1   -2 -1236                            $ Fuel

1742  2   0.055323      1   -2  1236 -1237                      $ Clad

1743  3   0.10018       1   -2    23   -24    78   -79  1237    $ Water

1744  1   0.068525      1   -2 -1238                            $ Fuel

1745  2   0.055323      1   -2  1238 -1239                      $ Clad

1746  3   0.10018       1   -2    23   -24    79   -80  1239    $ Water

1747  1   0.068525      1   -2 -1240                            $ Fuel

1748  2   0.055323      1   -2  1240 -1241                      $ Clad

1749  3   0.10018       1   -2    23   -24    80   -81  1241    $ Water

1750  1   0.068525      1   -2 -1242                            $ Fuel

1751  2   0.055323      1   -2  1242 -1243                      $ Clad

1752  3   0.10018       1   -2    23   -24    81   -82  1243    $ Water

1753  3   0.10018       1   -2    23   -24    82    -5          $ Reflector

1754  1   0.068525      1   -2 -1244                            $ Fuel

1755  2   0.055323      1   -2  1244 -1245                      $ Clad

1756  3   0.10018       1   -2    24   -25    69   -70  1245    $ Water

1757  1   0.068525      1   -2 -1246                            $ Fuel

1758  2   0.055323      1   -2  1246 -1247                      $ Clad

1759  3   0.10018       1   -2    24   -25    70   -71  1247    $ Water

1760  1   0.068525      1   -2 -1248                            $ Fuel

1761  2   0.055323      1   -2  1248 -1249                      $ Clad

1762  3   0.10018       1   -2    24   -25    71   -72  1249    $ Water

1763  1   0.068525      1   -2 -1250                            $ Fuel

1764  2   0.055323      1   -2  1250 -1251                      $ Clad

1765  3   0.10018       1   -2    24   -25    72   -73  1251    $ Water

1766  1   0.068525      1   -2 -1252                            $ Fuel

1767  2   0.055323      1   -2  1252 -1253                      $ Clad

1768  3   0.10018       1   -2    24   -25    73   -74  1253    $ Water

1769  1   0.068525      1   -2 -1254                            $ Fuel

1770  2   0.055323      1   -2  1254 -1255                      $ Clad

1771  3   0.10018       1   -2    24   -25    74   -75  1255    $ Water

1772  1   0.068525      1   -2 -1256                            $ Fuel

1773  2   0.055323      1   -2  1256 -1257                      $ Clad

1774  3   0.10018       1   -2    24   -25    75   -76  1257    $ Water

1775  1   0.068525      1   -2 -1258                            $ Fuel

1776  2   0.055323      1   -2  1258 -1259                      $ Clad

1777  3   0.10018       1   -2    24   -25    76   -77  1259    $ Water

1778  1   0.068525      1   -2 -1260                            $ Fuel

1779  2   0.055323      1   -2  1260 -1261                      $ Clad

1780  3   0.10018       1   -2    24   -25    77   -78  1261    $ Water

1781  1   0.068525      1   -2 -1262                            $ Fuel

1782  2   0.055323      1   -2  1262 -1263                      $ Clad

1783  3   0.10018       1   -2    24   -25    78   -79  1263    $ Water

1784  1   0.068525      1   -2 -1264                            $ Fuel

1785  2   0.055323      1   -2  1264 -1265                      $ Clad

1786  3   0.10018       1   -2    24   -25    79   -80  1265    $ Water

1787  1   0.068525      1   -2 -1266                            $ Fuel

1788  2   0.055323      1   -2  1266 -1267                      $ Clad

1789  3   0.10018       1   -2    24   -25    80   -81  1267    $ Water

1790  1   0.068525      1   -2 -1268                            $ Fuel

1791  2   0.055323      1   -2  1268 -1269                      $ Clad

1792  3   0.10018       1   -2    24   -25    81   -82  1269    $ Water

1793  3   0.10018       1   -2    24   -25    82    -5          $ Reflector

1794  1   0.068525      1   -2 -1270                            $ Fuel

1795  2   0.055323      1   -2  1270 -1271                      $ Clad

1796  3   0.10018       1   -2    25   -26    69   -70  1271    $ Water

1797  1   0.068525      1   -2 -1272                            $ Fuel

1798  2   0.055323      1   -2  1272 -1273                      $ Clad

1799  3   0.10018       1   -2    25   -26    70   -71  1273    $ Water

1800  1   0.068525      1   -2 -1274                            $ Fuel

1801  2   0.055323      1   -2  1274 -1275                      $ Clad

1802  3   0.10018       1   -2    25   -26    71   -72  1275    $ Water

1803  1   0.068525      1   -2 -1276                            $ Fuel

1804  2   0.055323      1   -2  1276 -1277                      $ Clad

1805  3   0.10018       1   -2    25   -26    72   -73  1277    $ Water

1806  1   0.068525      1   -2 -1278                            $ Fuel

1807  2   0.055323      1   -2  1278 -1279                      $ Clad

1808  3   0.10018       1   -2    25   -26    73   -74  1279    $ Water

1809  1   0.068525      1   -2 -1280                            $ Fuel

1810  2   0.055323      1   -2  1280 -1281                      $ Clad

1811  3   0.10018       1   -2    25   -26    74   -75  1281    $ Water

1812  1   0.068525      1   -2 -1282                            $ Fuel

1813  2   0.055323      1   -2  1282 -1283                      $ Clad

1814  3   0.10018       1   -2    25   -26    75   -76  1283    $ Water

1815  1   0.068525      1   -2 -1284                            $ Fuel

1816  2   0.055323      1   -2  1284 -1285                      $ Clad

1817  3   0.10018       1   -2    25   -26    76   -77  1285    $ Water

1818  1   0.068525      1   -2 -1286                            $ Fuel

1819  2   0.055323      1   -2  1286 -1287                      $ Clad

1820  3   0.10018       1   -2    25   -26    77   -78  1287    $ Water

1821  1   0.068525      1   -2 -1288                            $ Fuel

1822  2   0.055323      1   -2  1288 -1289                      $ Clad

1823  3   0.10018       1   -2    25   -26    78   -79  1289    $ Water

1824  1   0.068525      1   -2 -1290                            $ Fuel

1825  2   0.055323      1   -2  1290 -1291                      $ Clad

1826  3   0.10018       1   -2    25   -26    79   -80  1291    $ Water

1827  1   0.068525      1   -2 -1292                            $ Fuel

1828  2   0.055323      1   -2  1292 -1293                      $ Clad

1829  3   0.10018       1   -2    25   -26    80   -81  1293    $ Water

1830  1   0.068525      1   -2 -1294                            $ Fuel

1831  2   0.055323      1   -2  1294 -1295                      $ Clad

1832  3   0.10018       1   -2    25   -26    81   -82  1295    $ Water

1833  3   0.10018       1   -2    25   -26    82    -5          $ Reflector

1834  1   0.068525      1   -2 -1296                            $ Fuel

1835  2   0.055323      1   -2  1296 -1297                      $ Clad

1836  3   0.10018       1   -2    26   -27    69   -70  1297    $ Water

1837  1   0.068525      1   -2 -1298                            $ Fuel

1838  2   0.055323      1   -2  1298 -1299                      $ Clad

1839  3   0.10018       1   -2    26   -27    70   -71  1299    $ Water

1840  1   0.068525      1   -2 -1300                            $ Fuel

1841  2   0.055323      1   -2  1300 -1301                      $ Clad

1842  3   0.10018       1   -2    26   -27    71   -72  1301    $ Water

1843  1   0.068525      1   -2 -1302                            $ Fuel

1844  2   0.055323      1   -2  1302 -1303                      $ Clad

1845  3   0.10018       1   -2    26   -27    72   -73  1303    $ Water

1846  1   0.068525      1   -2 -1304                            $ Fuel

1847  2   0.055323      1   -2  1304 -1305                      $ Clad

1848  3   0.10018       1   -2    26   -27    73   -74  1305    $ Water

1849  1   0.068525      1   -2 -1306                            $ Fuel

1850  2   0.055323      1   -2  1306 -1307                      $ Clad

1851  3   0.10018       1   -2    26   -27    74   -75  1307    $ Water

1852  1   0.068525      1   -2 -1308                            $ Fuel

1853  2   0.055323      1   -2  1308 -1309                      $ Clad

1854  3   0.10018       1   -2    26   -27    75   -76  1309    $ Water

1855  1   0.068525      1   -2 -1310                            $ Fuel

1856  2   0.055323      1   -2  1310 -1311                      $ Clad

1857  3   0.10018       1   -2    26   -27    76   -77  1311    $ Water

1858  3   0.10018       1   -2    26   -27    77    -5          $ Reflector

1859  1   0.068525      1   -2 -1312                            $ Fuel

1860  2   0.055323      1   -2  1312 -1313                      $ Clad

1861  3   0.10018       1   -2    27   -28    69   -70  1313    $ Water

1862  1   0.068525      1   -2 -1314                            $ Fuel

1863  2   0.055323      1   -2  1314 -1315                      $ Clad

1864  3   0.10018       1   -2    27   -28    70   -71  1315    $ Water

1865  1   0.068525      1   -2 -1316                            $ Fuel

1866  2   0.055323      1   -2  1316 -1317                      $ Clad

1867  3   0.10018       1   -2    27   -28    71   -72  1317    $ Water

1868  1   0.068525      1   -2 -1318                            $ Fuel

1869  2   0.055323      1   -2  1318 -1319                      $ Clad

1870  3   0.10018       1   -2    27   -28    72   -73  1319    $ Water

1871  1   0.068525      1   -2 -1320                            $ Fuel

1872  2   0.055323      1   -2  1320 -1321                      $ Clad

1873  3   0.10018       1   -2    27   -28    73   -74  1321    $ Water

1874  1   0.068525      1   -2 -1322                            $ Fuel

1875  2   0.055323      1   -2  1322 -1323                      $ Clad

1876  3   0.10018       1   -2    27   -28    74   -75  1323    $ Water

1877  1   0.068525      1   -2 -1324                            $ Fuel

1878  2   0.055323      1   -2  1324 -1325                      $ Clad

1879  3   0.10018       1   -2    27   -28    75   -76  1325    $ Water

1880  1   0.068525      1   -2 -1326                            $ Fuel

1881  2   0.055323      1   -2  1326 -1327                      $ Clad

1882  3   0.10018       1   -2    27   -28    76   -77  1327    $ Water

1883  3   0.10018       1   -2    27   -28    77    -5          $ Reflector

1884  1   0.068525      1   -2     4 -1328                      $ Fuel

1885  2   0.055323      1   -2     4  1328 -1329                $ Clad

1886  3   0.10018       1   -2     4    28    69   -70  1329    $ Water

1887  1   0.068525      1   -2 -1330                            $ Fuel

1888  2   0.055323      1   -2  1330 -1331                      $ Clad

1889  3   0.10018       1   -2    28   -29    70   -71  1331    $ Water

1890  1   0.068525      1   -2 -1332                            $ Fuel

1891  2   0.055323      1   -2  1332 -1333                      $ Clad

1892  3   0.10018       1   -2    28   -29    71   -72  1333    $ Water

1893  1   0.068525      1   -2 -1334                            $ Fuel

1894  2   0.055323      1   -2  1334 -1335                      $ Clad

1895  3   0.10018       1   -2    28   -29    72   -73  1335    $ Water

1896  1   0.068525      1   -2 -1336                            $ Fuel

1897  2   0.055323      1   -2  1336 -1337                      $ Clad

1898  3   0.10018       1   -2    28   -29    73   -74  1337    $ Water

1899  1   0.068525      1   -2 -1338                            $ Fuel

1900  2   0.055323      1   -2  1338 -1339                      $ Clad

1901  3   0.10018       1   -2    28   -29    74   -75  1339    $ Water

1902  1   0.068525      1   -2 -1340                            $ Fuel

1903  2   0.055323      1   -2  1340 -1341                      $ Clad

1904  3   0.10018       1   -2    28   -29    75   -76  1341    $ Water

1905  1   0.068525      1   -2 -1342                            $ Fuel

1906  2   0.055323      1   -2  1342 -1343                      $ Clad

1907  3   0.10018       1   -2    28   -29    76   -77  1343    $ Water

1908  3   0.10018       1   -2    28   -29    77    -5          $ Reflector

1909  1   0.068525      1   -2     4 -1344                      $ Fuel

1910  2   0.055323      1   -2     4  1344 -1345                $ Clad

1911  3   0.10018       1   -2     4    29    70   -71  1345    $ Water

1912  1   0.068525      1   -2 -1346                            $ Fuel

1913  2   0.055323      1   -2  1346 -1347                      $ Clad

1914  3   0.10018       1   -2    29   -30    71   -72  1347    $ Water

1915  1   0.068525      1   -2 -1348                            $ Fuel

1916  2   0.055323      1   -2  1348 -1349                      $ Clad

1917  3   0.10018       1   -2    29   -30    72   -73  1349    $ Water

1918  1   0.068525      1   -2 -1350                            $ Fuel

1919  2   0.055323      1   -2  1350 -1351                      $ Clad

1920  3   0.10018       1   -2    29   -30    73   -74  1351    $ Water

1921  1   0.068525      1   -2 -1352                            $ Fuel

1922  2   0.055323      1   -2  1352 -1353                      $ Clad

1923  3   0.10018       1   -2    29   -30    74   -75  1353    $ Water

1924  1   0.068525      1   -2 -1354                            $ Fuel

1925  2   0.055323      1   -2  1354 -1355                      $ Clad

1926  3   0.10018       1   -2    29   -30    75   -76  1355    $ Water

1927  1   0.068525      1   -2 -1356                            $ Fuel

1928  2   0.055323      1   -2  1356 -1357                      $ Clad

1929  3   0.10018       1   -2    29   -30    76   -77  1357    $ Water

1930  3   0.10018       1   -2    29   -30    77    -5          $ Reflector

1931  1   0.068525      1   -2     4 -1358                      $ Fuel

1932  2   0.055323      1   -2     4  1358 -1359                $ Clad

1933  3   0.10018       1   -2     4    30    71   -72  1359    $ Water

1934  1   0.068525      1   -2 -1360                            $ Fuel

1935  2   0.055323      1   -2  1360 -1361                      $ Clad

1936  3   0.10018       1   -2    30   -31    72   -73  1361    $ Water

1937  1   0.068525      1   -2 -1362                            $ Fuel

1938  2   0.055323      1   -2  1362 -1363                      $ Clad

1939  3   0.10018       1   -2    30   -31    73   -74  1363    $ Water

1940  1   0.068525      1   -2 -1364                            $ Fuel

1941  2   0.055323      1   -2  1364 -1365                      $ Clad

1942  3   0.10018       1   -2    30   -31    74   -75  1365    $ Water

1943  1   0.068525      1   -2 -1366                            $ Fuel

1944  2   0.055323      1   -2  1366 -1367                      $ Clad

1945  3   0.10018       1   -2    30   -31    75   -76  1367    $ Water

1946  1   0.068525      1   -2 -1368                            $ Fuel

1947  2   0.055323      1   -2  1368 -1369                      $ Clad

1948  3   0.10018       1   -2    30   -31    76   -77  1369    $ Water

1949  3   0.10018       1   -2    30   -31    77    -5          $ Reflector

1950  1   0.068525      1   -2     4 -1370                      $ Fuel

1951  2   0.055323      1   -2     4  1370 -1371                $ Clad

1952  3   0.10018       1   -2     4    31    72   -73  1371    $ Water

1953  1   0.068525      1   -2 -1372                            $ Fuel

1954  2   0.055323      1   -2  1372 -1373                      $ Clad

1955  3   0.10018       1   -2    31   -32    73   -74  1373    $ Water

1956  1   0.068525      1   -2 -1374                            $ Fuel

1957  2   0.055323      1   -2  1374 -1375                      $ Clad

1958  3   0.10018       1   -2    31   -32    74   -75  1375    $ Water

1959  1   0.068525      1   -2 -1376                            $ Fuel

1960  2   0.055323      1   -2  1376 -1377                      $ Clad

1961  3   0.10018       1   -2    31   -32    75   -76  1377    $ Water

1962  1   0.068525      1   -2 -1378                            $ Fuel

1963  2   0.055323      1   -2  1378 -1379                      $ Clad

1964  3   0.10018       1   -2    31   -32    76   -77  1379    $ Water

1965  3   0.10018       1   -2    31   -32    77    -5          $ Reflector

1966  1   0.068525      1   -2     4 -1380                      $ Fuel

1967  2   0.055323      1   -2     4  1380 -1381                $ Clad

1968  3   0.10018       1   -2     4    32    73   -74  1381    $ Water

1969  1   0.068525      1   -2 -1382                            $ Fuel

1970  2   0.055323      1   -2  1382 -1383                      $ Clad

1971  3   0.10018       1   -2    32   -33    74   -75  1383    $ Water

1972  1   0.068525      1   -2 -1384                            $ Fuel

1973  2   0.055323      1   -2  1384 -1385                      $ Clad

1974  3   0.10018       1   -2    32   -33    75   -76  1385    $ Water

1975  1   0.068525      1   -2 -1386                            $ Fuel

1976  2   0.055323      1   -2  1386 -1387                      $ Clad

1977  3   0.10018       1   -2    32   -33    76   -77  1387    $ Water

1978  3   0.10018       1   -2    32   -33    77    -5          $ Reflector

1979  1   0.068525      1   -2     4 -1388                      $ Fuel

1980  2   0.055323      1   -2     4  1388 -1389                $ Clad

1981  3   0.10018       1   -2     4    33    74   -75  1389    $ Water

1982  1   0.068525      1   -2 -1390                            $ Fuel

1983  2   0.055323      1   -2  1390 -1391                      $ Clad

1984  3   0.10018       1   -2    33   -34    75   -76  1391    $ Water

1985  1   0.068525      1   -2 -1392                            $ Fuel

1986  2   0.055323      1   -2  1392 -1393                      $ Clad

1987  3   0.10018       1   -2    33   -34    76   -77  1393    $ Water

1988  3   0.10018       1   -2    33   -34    77    -5          $ Reflector

1989  1   0.068525      1   -2     4 -1394                      $ Fuel

1990  2   0.055323      1   -2     4  1394 -1395                $ Clad

1991  3   0.10018       1   -2     4    34    75   -76  1395    $ Water

1992  1   0.068525      1   -2 -1396                            $ Fuel

1993  2   0.055323      1   -2  1396 -1397                      $ Clad

1994  3   0.10018       1   -2    34   -35    76   -77  1397    $ Water

1995  3   0.10018       1   -2    34   -35    77    -5          $ Reflector

1996  1   0.068525      1   -2     4 -1398                      $ Fuel

1997  2   0.055323      1   -2     4  1398 -1399                $ Clad

1998  3   0.10018       1   -2     4    35    76   -77  1399    $ Water

1999  3   0.10018       1   -2     4    35   -36    77    -5    $ Reflector

2000  3   0.10018       1   -2     4    -5    36   -37    77    $ Reflector

2001  3   0.10018       1   -2     4    -5    37   -38    77    $ Reflector

2002  3   0.10018       1   -2     4    -5    38    77          $ Reflector

2003  0                 -1:2:-3:-4:5

1     pz    -81.662

2     pz     81.662

*3    py      0.0

*4    p       1.0    -1.0     0.0     0.0

5     cz     76.200

c    Cell Boundaries

6     py      0.81788

7     py      2.45364

8     py      4.08940

9     py      5.72516

10    py      7.36092

11    py      8.99668

12    py     10.63244

13    py     12.26820

14    py     13.90396

15    py     15.53972

16    py     17.17548

17    py     18.81124

18    py     20.44700

19    py     22.08276

20    py     23.71852

21    py     25.35428

22    py     26.99004

23    py     28.62580

24    py     30.26156

25    py     31.89732

26    py     33.53308

27    py     35.16884

28    py     36.80460

29    py     38.44036

30    py     40.07612

31    py     41.71188

32    py     43.34764

33    py     44.98340

34    py     46.61916

35    py     48.25492

36    py     49.89068

37    py     51.52644

38    py     53.16220

39    py     54.79796

40    py     56.43372

41    py     58.06948

42    py     59.70524

43    py     61.34100

44    py     62.97676

45    py     64.61252

46    py     66.24828

47    px      0.81788

48    px      2.45364

49    px      4.08940

50    px      5.72516

51    px      7.36092

52    px      8.99668

53    px     10.63244

54    px     12.26820

55    px     13.90396

56    px     15.53972

57    px     17.17548

58    px     18.81124

59    px     20.44700

60    px     22.08276

61    px     23.71852

62    px     25.35428

63    px     26.99004

64    px     28.62580

65    px     30.26156

66    px     31.89732

67    px     33.53308

68    px     35.16884

69    px     36.80460

70    px     38.44036

71    px     40.07612

72    px     41.71188

73    px     43.34764

74    px     44.98340

75    px     46.61916

76    px     48.25492

77    px     49.89068

78    px     51.52644

79    px     53.16220

80    px     54.79796

81    px     56.43372

82    px     58.06948

83    px     59.70524

84    px     61.34100

85    px     62.97676

86    px     64.61252

87    px     66.24828

c    Pins and Clad for Central Assembly

88    cz      0.514858

89    cz      0.602996

90    c/z     1.63576   0.0       0.514858

91    c/z     1.63576   0.0       0.602996

92    c/z     3.27152   0.0       0.514858

93    c/z     3.27152   0.0       0.602996

94    c/z     4.90728   0.0       0.514858

95    c/z     4.90728   0.0       0.602996

96    c/z     6.54304   0.0       0.514858

97    c/z     6.54304   0.0       0.602996

98    c/z     8.17880   0.0       0.514858

99    c/z     8.17880   0.0       0.602996

100   c/z     9.81456   0.0       0.514858

101   c/z     9.81456   0.0       0.602996

102   c/z    11.45032   0.0       0.514858

103   c/z    11.45032   0.0       0.602996

104   c/z     1.63576   1.63576   0.514858

105   c/z     1.63576   1.63576   0.602996

106   c/z     3.27152   1.63576   0.514858

107   c/z     3.27152   1.63576   0.602996

108   c/z     4.90728   1.63576   0.514858

109   c/z     4.90728   1.63576   0.602996

110   c/z     6.54304   1.63576   0.514858

111   c/z     6.54304   1.63576   0.602996

112   c/z     8.17880   1.63576   0.514858

113   c/z     8.17880   1.63576   0.602996

114   c/z     9.81456   1.63576   0.514858

115   c/z     9.81456   1.63576   0.602996

116   c/z    11.45032   1.63576   0.514858

117   c/z    11.45032   1.63576   0.602996

118   c/z     3.27152   3.27152   0.514858

119   c/z     3.27152   3.27152   0.602996

120   c/z     4.90728   3.27152   0.514858

121   c/z     4.90728   3.27152   0.602996

122   c/z     6.54304   3.27152   0.514858

123   c/z     6.54304   3.27152   0.602996

124   c/z     8.17880   3.27152   0.514858

125   c/z     8.17880   3.27152   0.602996

126   c/z     9.81456   3.27152   0.514858

127   c/z     9.81456   3.27152   0.602996

128   c/z    11.45032   3.27152   0.514858

129   c/z    11.45032   3.27152   0.602996

130   c/z     4.90728   4.90728   0.514858

131   c/z     4.90728   4.90728   0.602996

132   c/z     6.54304   4.90728   0.514858

133   c/z     6.54304   4.90728   0.602996

134   c/z     8.17880   4.90728   0.514858

135   c/z     8.17880   4.90728   0.602996

136   c/z     9.81456   4.90728   0.514858

137   c/z     9.81456   4.90728   0.602996

138   c/z    11.45032   4.90728   0.514858

139   c/z    11.45032   4.90728   0.602996

140   c/z     6.54304   6.54304   0.514858

141   c/z     6.54304   6.54304   0.602996

142   c/z     8.17880   6.54304   0.514858

143   c/z     8.17880   6.54304   0.602996

144   c/z     9.81456   6.54304   0.514858

145   c/z     9.81456   6.54304   0.602996

146   c/z    11.45032   6.54304   0.514858

147   c/z    11.45032   6.54304   0.602996

148   c/z     8.17880   8.17880   0.514858

149   c/z     8.17880   8.17880   0.602996

150   c/z     9.81456   8.17880   0.514858

151   c/z     9.81456   8.17880   0.602996

152   c/z    11.45032   8.17880   0.514858

153   c/z    11.45032   8.17880   0.602996

154   c/z     9.81456   9.81456   0.514858

155   c/z     9.81456   9.81456   0.602996

156   c/z    11.45032   9.81456   0.514858

157   c/z    11.45032   9.81456   0.602996

158   c/z    11.45032  11.45032   0.514858

159   c/z    11.45032  11.45032   0.602996

c    Pins and Clad for Right Central Assembly

160   c/z    13.08608   0.0       0.514858

161   c/z    13.08608   0.0       0.602996

162   c/z    14.72184   0.0       0.514858

163   c/z    14.72184   0.0       0.602996

164   c/z    16.35760   0.0       0.514858

165   c/z    16.35760   0.0       0.602996

166   c/z    17.99336   0.0       0.514858

167   c/z    17.99336   0.0       0.602996

168   c/z    19.62912   0.0       0.514858

169   c/z    19.62912   0.0       0.602996

170   c/z    21.26488   0.0       0.514858

171   c/z    21.26488   0.0       0.602996

172   c/z    22.90064   0.0       0.514858

173   c/z    22.90064   0.0       0.602996

174   c/z    24.53640   0.0       0.514858

175   c/z    24.53640   0.0       0.602996

176   c/z    26.17216   0.0       0.514858

177   c/z    26.17216   0.0       0.602996

178   c/z    27.80792   0.0       0.514858

179   c/z    27.80792   0.0       0.602996

180   c/z    29.44368   0.0       0.514858

181   c/z    29.44368   0.0       0.602996

182   c/z    31.07944   0.0       0.514858

183   c/z    31.07944   0.0       0.602996

184   c/z    32.71520   0.0       0.514858

185   c/z    32.71520   0.0       0.602996

186   c/z    34.35096   0.0       0.514858

187   c/z    34.35096   0.0       0.602996

188   c/z    35.98672   0.0       0.514858

189   c/z    35.98672   0.0       0.602996

190   c/z    13.08608   1.63576   0.514858

191   c/z    13.08608   1.63576   0.602996

192   c/z    14.72184   1.63576   0.514858

193   c/z    14.72184   1.63576   0.602996

194   c/z    16.35760   1.63576   0.514858

195   c/z    16.35760   1.63576   0.602996

196   c/z    17.99336   1.63576   0.514858

197   c/z    17.99336   1.63576   0.602996

198   c/z    19.62912   1.63576   0.514858

199   c/z    19.62912   1.63576   0.602996

200   c/z    21.26488   1.63576   0.514858

201   c/z    21.26488   1.63576   0.602996

202   c/z    22.90064   1.63576   0.514858

203   c/z    22.90064   1.63576   0.602996

204   c/z    24.53640   1.63576   0.514858

205   c/z    24.53640   1.63576   0.602996

206   c/z    26.17216   1.63576   0.514858

207   c/z    26.17216   1.63576   0.602996

208   c/z    27.80792   1.63576   0.514858

209   c/z    27.80792   1.63576   0.602996

210   c/z    29.44368   1.63576   0.514858

211   c/z    29.44368   1.63576   0.602996

212   c/z    31.07944   1.63576   0.514858

213   c/z    31.07944   1.63576   0.602996

214   c/z    32.71520   1.63576   0.514858

215   c/z    32.71520   1.63576   0.602996

216   c/z    34.35096   1.63576   0.514858

217   c/z    34.35096   1.63576   0.602996

218   c/z    35.98672   1.63576   0.514858

219   c/z    35.98672   1.63576   0.602996

220   c/z    13.08608   3.27152   0.514858

221   c/z    13.08608   3.27152   0.602996

222   c/z    14.72184   3.27152   0.514858

223   c/z    14.72184   3.27152   0.602996

224   c/z    16.35760   3.27152   0.514858

225   c/z    16.35760   3.27152   0.602996

226   c/z    17.99336   3.27152   0.514858

227   c/z    17.99336   3.27152   0.602996

228   c/z    19.62912   3.27152   0.514858

229   c/z    19.62912   3.27152   0.602996

230   c/z    21.26488   3.27152   0.514858

231   c/z    21.26488   3.27152   0.602996

232   c/z    22.90064   3.27152   0.514858

233   c/z    22.90064   3.27152   0.602996

234   c/z    24.53640   3.27152   0.514858

235   c/z    24.53640   3.27152   0.602996

236   c/z    26.17216   3.27152   0.514858

237   c/z    26.17216   3.27152   0.602996

238   c/z    27.80792   3.27152   0.514858

239   c/z    27.80792   3.27152   0.602996

240   c/z    29.44368   3.27152   0.514858

241   c/z    29.44368   3.27152   0.602996

242   c/z    31.07944   3.27152   0.514858

243   c/z    31.07944   3.27152   0.602996

244   c/z    32.71520   3.27152   0.514858

245   c/z    32.71520   3.27152   0.602996

246   c/z    34.35096   3.27152   0.514858

247   c/z    34.35096   3.27152   0.602996

248   c/z    35.98672   3.27152   0.514858

249   c/z    35.98672   3.27152   0.602996

250   c/z    13.08608   4.90728   0.514858

251   c/z    13.08608   4.90728   0.602996

252   c/z    14.72184   4.90728   0.514858

253   c/z    14.72184   4.90728   0.602996

254   c/z    16.35760   4.90728   0.514858

255   c/z    16.35760   4.90728   0.602996

256   c/z    17.99336   4.90728   0.514858

257   c/z    17.99336   4.90728   0.602996

258   c/z    19.62912   4.90728   0.514858

259   c/z    19.62912   4.90728   0.602996

260   c/z    21.26488   4.90728   0.514858

261   c/z    21.26488   4.90728   0.602996

262   c/z    22.90064   4.90728   0.514858

263   c/z    22.90064   4.90728   0.602996

264   c/z    24.53640   4.90728   0.514858

265   c/z    24.53640   4.90728   0.602996

266   c/z    26.17216   4.90728   0.514858

267   c/z    26.17216   4.90728   0.602996

268   c/z    27.80792   4.90728   0.514858

269   c/z    27.80792   4.90728   0.602996

270   c/z    29.44368   4.90728   0.514858

271   c/z    29.44368   4.90728   0.602996

272   c/z    31.07944   4.90728   0.514858

273   c/z    31.07944   4.90728   0.602996

274   c/z    32.71520   4.90728   0.514858

275   c/z    32.71520   4.90728   0.602996

276   c/z    34.35096   4.90728   0.514858

277   c/z    34.35096   4.90728   0.602996

278   c/z    35.98672   4.90728   0.514858

279   c/z    35.98672   4.90728   0.602996

280   c/z    13.08608   6.54304   0.514858

281   c/z    13.08608   6.54304   0.602996

282   c/z    14.72184   6.54304   0.514858

283   c/z    14.72184   6.54304   0.602996

284   c/z    16.35760   6.54304   0.514858

285   c/z    16.35760   6.54304   0.602996

286   c/z    17.99336   6.54304   0.514858

287   c/z    17.99336   6.54304   0.602996

288   c/z    19.62912   6.54304   0.514858

289   c/z    19.62912   6.54304   0.602996

290   c/z    21.26488   6.54304   0.514858

291   c/z    21.26488   6.54304   0.602996

292   c/z    22.90064   6.54304   0.514858

293   c/z    22.90064   6.54304   0.602996

294   c/z    24.53640   6.54304   0.514858

295   c/z    24.53640   6.54304   0.602996

296   c/z    26.17216   6.54304   0.514858

297   c/z    26.17216   6.54304   0.602996

298   c/z    27.80792   6.54304   0.514858

299   c/z    27.80792   6.54304   0.602996

300   c/z    29.44368   6.54304   0.514858

301   c/z    29.44368   6.54304   0.602996

302   c/z    31.07944   6.54304   0.514858

303   c/z    31.07944   6.54304   0.602996

304   c/z    32.71520   6.54304   0.514858

305   c/z    32.71520   6.54304   0.602996

306   c/z    34.35096   6.54304   0.514858

307   c/z    34.35096   6.54304   0.602996

308   c/z    35.98672   6.54304   0.514858

309   c/z    35.98672   6.54304   0.602996

310   c/z    13.08608   8.17880   0.514858

311   c/z    13.08608   8.17880   0.602996

312   c/z    14.72184   8.17880   0.514858

313   c/z    14.72184   8.17880   0.602996

314   c/z    16.35760   8.17880   0.514858

315   c/z    16.35760   8.17880   0.602996

316   c/z    17.99336   8.17880   0.514858

317   c/z    17.99336   8.17880   0.602996

318   c/z    19.62912   8.17880   0.514858

319   c/z    19.62912   8.17880   0.602996

320   c/z    21.26488   8.17880   0.514858

321   c/z    21.26488   8.17880   0.602996

322   c/z    22.90064   8.17880   0.514858

323   c/z    22.90064   8.17880   0.602996

324   c/z    24.53640   8.17880   0.514858

325   c/z    24.53640   8.17880   0.602996

326   c/z    26.17216   8.17880   0.514858

327   c/z    26.17216   8.17880   0.602996

328   c/z    27.80792   8.17880   0.514858

329   c/z    27.80792   8.17880   0.602996

330   c/z    29.44368   8.17880   0.514858

331   c/z    29.44368   8.17880   0.602996

332   c/z    31.07944   8.17880   0.514858

333   c/z    31.07944   8.17880   0.602996

334   c/z    32.71520   8.17880   0.514858

335   c/z    32.71520   8.17880   0.602996

336   c/z    34.35096   8.17880   0.514858

337   c/z    34.35096   8.17880   0.602996

338   c/z    35.98672   8.17880   0.514858

339   c/z    35.98672   8.17880   0.602996

340   c/z    13.08608   9.81456   0.514858

341   c/z    13.08608   9.81456   0.602996

342   c/z    14.72184   9.81456   0.514858

343   c/z    14.72184   9.81456   0.602996

344   c/z    16.35760   9.81456   0.514858

345   c/z    16.35760   9.81456   0.602996

346   c/z    17.99336   9.81456   0.514858

347   c/z    17.99336   9.81456   0.602996

348   c/z    19.62912   9.81456   0.514858

349   c/z    19.62912   9.81456   0.602996

350   c/z    21.26488   9.81456   0.514858

351   c/z    21.26488   9.81456   0.602996

352   c/z    22.90064   9.81456   0.514858

353   c/z    22.90064   9.81456   0.602996

354   c/z    24.53640   9.81456   0.514858

355   c/z    24.53640   9.81456   0.602996

356   c/z    26.17216   9.81456   0.514858

357   c/z    26.17216   9.81456   0.602996

358   c/z    27.80792   9.81456   0.514858

359   c/z    27.80792   9.81456   0.602996

360   c/z    29.44368   9.81456   0.514858

361   c/z    29.44368   9.81456   0.602996

362   c/z    31.07944   9.81456   0.514858

363   c/z    31.07944   9.81456   0.602996

364   c/z    32.71520   9.81456   0.514858

365   c/z    32.71520   9.81456   0.602996

366   c/z    34.35096   9.81456   0.514858

367   c/z    34.35096   9.81456   0.602996

368   c/z    35.98672   9.81456   0.514858

369   c/z    35.98672   9.81456   0.602996

370   c/z    13.08608  11.45032   0.514858

371   c/z    13.08608  11.45032   0.602996

372   c/z    14.72184  11.45032   0.514858

373   c/z    14.72184  11.45032   0.602996

374   c/z    16.35760  11.45032   0.514858

375   c/z    16.35760  11.45032   0.602996

376   c/z    17.99336  11.45032   0.514858

377   c/z    17.99336  11.45032   0.602996

378   c/z    19.62912  11.45032   0.514858

379   c/z    19.62912  11.45032   0.602996

380   c/z    21.26488  11.45032   0.514858

381   c/z    21.26488  11.45032   0.602996

382   c/z    22.90064  11.45032   0.514858

383   c/z    22.90064  11.45032   0.602996

384   c/z    24.53640  11.45032   0.514858

385   c/z    24.53640  11.45032   0.602996

386   c/z    26.17216  11.45032   0.514858

387   c/z    26.17216  11.45032   0.602996

388   c/z    27.80792  11.45032   0.514858

389   c/z    27.80792  11.45032   0.602996

390   c/z    29.44368  11.45032   0.514858

391   c/z    29.44368  11.45032   0.602996

392   c/z    31.07944  11.45032   0.514858

393   c/z    31.07944  11.45032   0.602996

394   c/z    32.71520  11.45032   0.514858

395   c/z    32.71520  11.45032   0.602996

396   c/z    34.35096  11.45032   0.514858

397   c/z    34.35096  11.45032   0.602996

398   c/z    35.98672  11.45032   0.514858

399   c/z    35.98672  11.45032   0.602996

c    Pins and Clad for Upper Right Assembly

400   c/z    13.08608  13.08608   0.514858

401   c/z    13.08608  13.08608   0.602996

402   c/z    14.72184  13.08608   0.514858

403   c/z    14.72184  13.08608   0.602996

404   c/z    16.35760  13.08608   0.514858

405   c/z    16.35760  13.08608   0.602996

406   c/z    17.99336  13.08608   0.514858

407   c/z    17.99336  13.08608   0.602996

408   c/z    19.62912  13.08608   0.514858

409   c/z    19.62912  13.08608   0.602996

410   c/z    21.26488  13.08608   0.514858

411   c/z    21.26488  13.08608   0.602996

412   c/z    22.90064  13.08608   0.514858

413   c/z    22.90064  13.08608   0.602996

414   c/z    24.53640  13.08608   0.514858

415   c/z    24.53640  13.08608   0.602996

416   c/z    26.17216  13.08608   0.514858

417   c/z    26.17216  13.08608   0.602996

418   c/z    27.80792  13.08608   0.514858

419   c/z    27.80792  13.08608   0.602996

420   c/z    29.44368  13.08608   0.514858

421   c/z    29.44368  13.08608   0.602996

422   c/z    31.07944  13.08608   0.514858

423   c/z    31.07944  13.08608   0.602996

424   c/z    32.71520  13.08608   0.514858

425   c/z    32.71520  13.08608   0.602996

426   c/z    34.35096  13.08608   0.514858

427   c/z    34.35096  13.08608   0.602996

428   c/z    35.98672  13.08608   0.514858

429   c/z    35.98672  13.08608   0.602996

430   c/z    14.72184  14.72184   0.514858

431   c/z    14.72184  14.72184   0.602996

432   c/z    16.35760  14.72184   0.514858

433   c/z    16.35760  14.72184   0.602996

434   c/z    17.99336  14.72184   0.514858

435   c/z    17.99336  14.72184   0.602996

436   c/z    19.62912  14.72184   0.514858

437   c/z    19.62912  14.72184   0.602996

438   c/z    21.26488  14.72184   0.514858

439   c/z    21.26488  14.72184   0.602996

440   c/z    22.90064  14.72184   0.514858

441   c/z    22.90064  14.72184   0.602996

442   c/z    24.53640  14.72184   0.514858

443   c/z    24.53640  14.72184   0.602996

444   c/z    26.17216  14.72184   0.514858

445   c/z    26.17216  14.72184   0.602996

446   c/z    27.80792  14.72184   0.514858

447   c/z    27.80792  14.72184   0.602996

448   c/z    29.44368  14.72184   0.514858

449   c/z    29.44368  14.72184   0.602996

450   c/z    31.07944  14.72184   0.514858

451   c/z    31.07944  14.72184   0.602996

452   c/z    32.71520  14.72184   0.514858

453   c/z    32.71520  14.72184   0.602996

454   c/z    34.35096  14.72184   0.514858

455   c/z    34.35096  14.72184   0.602996

456   c/z    35.98672  14.72184   0.514858

457   c/z    35.98672  14.72184   0.602996

458   c/z    16.35760  16.35760   0.514858

459   c/z    16.35760  16.35760   0.602996

460   c/z    17.99336  16.35760   0.514858

461   c/z    17.99336  16.35760   0.602996

462   c/z    19.62912  16.35760   0.514858

463   c/z    19.62912  16.35760   0.602996

464   c/z    21.26488  16.35760   0.514858

465   c/z    21.26488  16.35760   0.602996

466   c/z    22.90064  16.35760   0.514858

467   c/z    22.90064  16.35760   0.602996

468   c/z    24.53640  16.35760   0.514858

469   c/z    24.53640  16.35760   0.602996

470   c/z    26.17216  16.35760   0.514858

471   c/z    26.17216  16.35760   0.602996

472   c/z    27.80792  16.35760   0.514858

473   c/z    27.80792  16.35760   0.602996

474   c/z    29.44368  16.35760   0.514858

475   c/z    29.44368  16.35760   0.602996

476   c/z    31.07944  16.35760   0.514858

477   c/z    31.07944  16.35760   0.602996

478   c/z    32.71520  16.35760   0.514858

479   c/z    32.71520  16.35760   0.602996

480   c/z    34.35096  16.35760   0.514858

481   c/z    34.35096  16.35760   0.602996

482   c/z    35.98672  16.35760   0.514858

483   c/z    35.98672  16.35760   0.602996

484   c/z    17.99336  17.99336   0.514858

485   c/z    17.99336  17.99336   0.602996

486   c/z    19.62912  17.99336   0.514858

487   c/z    19.62912  17.99336   0.602996

488   c/z    21.26488  17.99336   0.514858

489   c/z    21.26488  17.99336   0.602996

490   c/z    22.90064  17.99336   0.514858

491   c/z    22.90064  17.99336   0.602996

492   c/z    24.53640  17.99336   0.514858

493   c/z    24.53640  17.99336   0.602996

494   c/z    26.17216  17.99336   0.514858

495   c/z    26.17216  17.99336   0.602996

496   c/z    27.80792  17.99336   0.514858

497   c/z    27.80792  17.99336   0.602996

498   c/z    29.44368  17.99336   0.514858

499   c/z    29.44368  17.99336   0.602996

500   c/z    31.07944  17.99336   0.514858

501   c/z    31.07944  17.99336   0.602996

502   c/z    32.71520  17.99336   0.514858

503   c/z    32.71520  17.99336   0.602996

504   c/z    34.35096  17.99336   0.514858

505   c/z    34.35096  17.99336   0.602996

506   c/z    35.98672  17.99336   0.514858

507   c/z    35.98672  17.99336   0.602996

508   c/z    19.62912  19.62912   0.514858

509   c/z    19.62912  19.62912   0.602996

510   c/z    21.26488  19.62912   0.514858

511   c/z    21.26488  19.62912   0.602996

512   c/z    22.90064  19.62912   0.514858

513   c/z    22.90064  19.62912   0.602996

514   c/z    24.53640  19.62912   0.514858

515   c/z    24.53640  19.62912   0.602996

516   c/z    26.17216  19.62912   0.514858

517   c/z    26.17216  19.62912   0.602996

518   c/z    27.80792  19.62912   0.514858

519   c/z    27.80792  19.62912   0.602996

520   c/z    29.44368  19.62912   0.514858

521   c/z    29.44368  19.62912   0.602996

522   c/z    31.07944  19.62912   0.514858

523   c/z    31.07944  19.62912   0.602996

524   c/z    32.71520  19.62912   0.514858

525   c/z    32.71520  19.62912   0.602996

526   c/z    34.35096  19.62912   0.514858

527   c/z    34.35096  19.62912   0.602996

528   c/z    35.98672  19.62912   0.514858

529   c/z    35.98672  19.62912   0.602996

530   c/z    21.26488  21.26488   0.514858

531   c/z    21.26488  21.26488   0.602996

532   c/z    22.90064  21.26488   0.514858

533   c/z    22.90064  21.26488   0.602996

534   c/z    24.53640  21.26488   0.514858

535   c/z    24.53640  21.26488   0.602996

536   c/z    26.17216  21.26488   0.514858

537   c/z    26.17216  21.26488   0.602996

538   c/z    27.80792  21.26488   0.514858

539   c/z    27.80792  21.26488   0.602996

540   c/z    29.44368  21.26488   0.514858

541   c/z    29.44368  21.26488   0.602996

542   c/z    31.07944  21.26488   0.514858

543   c/z    31.07944  21.26488   0.602996

544   c/z    32.71520  21.26488   0.514858

545   c/z    32.71520  21.26488   0.602996

546   c/z    34.35096  21.26488   0.514858

547   c/z    34.35096  21.26488   0.602996

548   c/z    35.98672  21.26488   0.514858

549   c/z    35.98672  21.26488   0.602996

550   c/z    22.90064  22.90064   0.514858

551   c/z    22.90064  22.90064   0.602996

552   c/z    24.53640  22.90064   0.514858

553   c/z    24.53640  22.90064   0.602996

554   c/z    26.17216  22.90064   0.514858

555   c/z    26.17216  22.90064   0.602996

556   c/z    27.80792  22.90064   0.514858

557   c/z    27.80792  22.90064   0.602996

558   c/z    29.44368  22.90064   0.514858

559   c/z    29.44368  22.90064   0.602996

560   c/z    31.07944  22.90064   0.514858

561   c/z    31.07944  22.90064   0.602996

562   c/z    32.71520  22.90064   0.514858

563   c/z    32.71520  22.90064   0.602996

564   c/z    34.35096  22.90064   0.514858

565   c/z    34.35096  22.90064   0.602996

566   c/z    35.98672  22.90064   0.514858

567   c/z    35.98672  22.90064   0.602996

568   c/z    24.53640  24.53640   0.514858

569   c/z    24.53640  24.53640   0.602996

570   c/z    26.17216  24.53640   0.514858

571   c/z    26.17216  24.53640   0.602996

572   c/z    27.80792  24.53640   0.514858

573   c/z    27.80792  24.53640   0.602996

574   c/z    29.44368  24.53640   0.514858

575   c/z    29.44368  24.53640   0.602996

576   c/z    31.07944  24.53640   0.514858

577   c/z    31.07944  24.53640   0.602996

578   c/z    32.71520  24.53640   0.514858

579   c/z    32.71520  24.53640   0.602996

580   c/z    34.35096  24.53640   0.514858

581   c/z    34.35096  24.53640   0.602996

582   c/z    35.98672  24.53640   0.514858

583   c/z    35.98672  24.53640   0.602996

584   c/z    26.17216  26.17216   0.514858

585   c/z    26.17216  26.17216   0.602996

586   c/z    27.80792  26.17216   0.514858

587   c/z    27.80792  26.17216   0.602996

588   c/z    29.44368  26.17216   0.514858

589   c/z    29.44368  26.17216   0.602996

590   c/z    31.07944  26.17216   0.514858

591   c/z    31.07944  26.17216   0.602996

592   c/z    32.71520  26.17216   0.514858

593   c/z    32.71520  26.17216   0.602996

594   c/z    34.35096  26.17216   0.514858

595   c/z    34.35096  26.17216   0.602996

596   c/z    35.98672  26.17216   0.514858

597   c/z    35.98672  26.17216   0.602996

598   c/z    27.80792  27.80792   0.514858

599   c/z    27.80792  27.80792   0.602996

600   c/z    29.44368  27.80792   0.514858

601   c/z    29.44368  27.80792   0.602996

602   c/z    31.07944  27.80792   0.514858

603   c/z    31.07944  27.80792   0.602996

604   c/z    32.71520  27.80792   0.514858

605   c/z    32.71520  27.80792   0.602996

606   c/z    34.35096  27.80792   0.514858

607   c/z    34.35096  27.80792   0.602996

608   c/z    35.98672  27.80792   0.514858

609   c/z    35.98672  27.80792   0.602996

610   c/z    29.44368  29.44368   0.514858

611   c/z    29.44368  29.44368   0.602996

612   c/z    31.07944  29.44368   0.514858

613   c/z    31.07944  29.44368   0.602996

614   c/z    32.71520  29.44368   0.514858

615   c/z    32.71520  29.44368   0.602996

616   c/z    34.35096  29.44368   0.514858

617   c/z    34.35096  29.44368   0.602996

618   c/z    35.98672  29.44368   0.514858

619   c/z    35.98672  29.44368   0.602996

620   c/z    31.07944  31.07944   0.514858

621   c/z    31.07944  31.07944   0.602996

622   c/z    32.71520  31.07944   0.514858

623   c/z    32.71520  31.07944   0.602996

624   c/z    34.35096  31.07944   0.514858

625   c/z    34.35096  31.07944   0.602996

626   c/z    35.98672  31.07944   0.514858

627   c/z    35.98672  31.07944   0.602996

628   c/z    32.71520  32.71520   0.514858

629   c/z    32.71520  32.71520   0.602996

630   c/z    34.35096  32.71520   0.514858

631   c/z    34.35096  32.71520   0.602996

632   c/z    35.98672  32.71520   0.514858

633   c/z    35.98672  32.71520   0.602996

634   c/z    34.35096  34.35096   0.514858

635   c/z    34.35096  34.35096   0.602996

636   c/z    35.98672  34.35096   0.514858

637   c/z    35.98672  34.35096   0.602996

638   c/z    35.98672  35.98672   0.514858

639   c/z    35.98672  35.98672   0.602996

c    Pins and Clad for Buffer

640   c/z    37.62248   0.0       0.514858

641   c/z    37.62248   0.0       0.602996

642   c/z    39.25824   0.0       0.514858

643   c/z    39.25824   0.0       0.602996

644   c/z    40.89400   0.0       0.514858

645   c/z    40.89400   0.0       0.602996

646   c/z    42.52976   0.0       0.514858

647   c/z    42.52976   0.0       0.602996

648   c/z    44.16552   0.0       0.514858

649   c/z    44.16552   0.0       0.602996

650   c/z    45.80128   0.0       0.514858

651   c/z    45.80128   0.0       0.602996

652   c/z    47.43704   0.0       0.514858

653   c/z    47.43704   0.0       0.602996

654   c/z    49.07280   0.0       0.514858

655   c/z    49.07280   0.0       0.602996

656   c/z    50.70856   0.0       0.514858

657   c/z    50.70856   0.0       0.602996

658   c/z    52.34432   0.0       0.514858

659   c/z    52.34432   0.0       0.602996

660   c/z    53.98008   0.0       0.514858

661   c/z    53.98008   0.0       0.602996

662   c/z    55.61584   0.0       0.514858

663   c/z    55.61584   0.0       0.602996

664   c/z    57.25160   0.0       0.514858

665   c/z    57.25160   0.0       0.602996

666   c/z    58.88736   0.0       0.514858

667   c/z    58.88736   0.0       0.602996

668   c/z    60.52312   0.0       0.514858

669   c/z    60.52312   0.0       0.602996

670   c/z    62.15888   0.0       0.514858

671   c/z    62.15888   0.0       0.602996

672   c/z    63.79464   0.0       0.514858

673   c/z    63.79464   0.0       0.602996

674   c/z    65.43040   0.0       0.514858

675   c/z    65.43040   0.0       0.602996

676   c/z    37.62248   1.63576   0.514858

677   c/z    37.62248   1.63576   0.602996

678   c/z    39.25824   1.63576   0.514858

679   c/z    39.25824   1.63576   0.602996

680   c/z    40.89400   1.63576   0.514858

681   c/z    40.89400   1.63576   0.602996

682   c/z    42.52976   1.63576   0.514858

683   c/z    42.52976   1.63576   0.602996

684   c/z    44.16552   1.63576   0.514858

685   c/z    44.16552   1.63576   0.602996

686   c/z    45.80128   1.63576   0.514858

687   c/z    45.80128   1.63576   0.602996

688   c/z    47.43704   1.63576   0.514858

689   c/z    47.43704   1.63576   0.602996

690   c/z    49.07280   1.63576   0.514858

691   c/z    49.07280   1.63576   0.602996

692   c/z    50.70856   1.63576   0.514858

693   c/z    50.70856   1.63576   0.602996

694   c/z    52.34432   1.63576   0.514858

695   c/z    52.34432   1.63576   0.602996

696   c/z    53.98008   1.63576   0.514858

697   c/z    53.98008   1.63576   0.602996

698   c/z    55.61584   1.63576   0.514858

699   c/z    55.61584   1.63576   0.602996

700   c/z    57.25160   1.63576   0.514858

701   c/z    57.25160   1.63576   0.602996

702   c/z    58.88736   1.63576   0.514858

703   c/z    58.88736   1.63576   0.602996

704   c/z    60.52312   1.63576   0.514858

705   c/z    60.52312   1.63576   0.602996

706   c/z    62.15888   1.63576   0.514858

707   c/z    62.15888   1.63576   0.602996

708   c/z    63.79464   1.63576   0.514858

709   c/z    63.79464   1.63576   0.602996

710   c/z    65.43040   1.63576   0.514858

711   c/z    65.43040   1.63576   0.602996

712   c/z    37.62248   3.27152   0.514858

713   c/z    37.62248   3.27152   0.602996

714   c/z    39.25824   3.27152   0.514858

715   c/z    39.25824   3.27152   0.602996

716   c/z    40.89400   3.27152   0.514858

717   c/z    40.89400   3.27152   0.602996

718   c/z    42.52976   3.27152   0.514858

719   c/z    42.52976   3.27152   0.602996

720   c/z    44.16552   3.27152   0.514858

721   c/z    44.16552   3.27152   0.602996

722   c/z    45.80128   3.27152   0.514858

723   c/z    45.80128   3.27152   0.602996

724   c/z    47.43704   3.27152   0.514858

725   c/z    47.43704   3.27152   0.602996

726   c/z    49.07280   3.27152   0.514858

727   c/z    49.07280   3.27152   0.602996

728   c/z    50.70856   3.27152   0.514858

729   c/z    50.70856   3.27152   0.602996

730   c/z    52.34432   3.27152   0.514858

731   c/z    52.34432   3.27152   0.602996

732   c/z    53.98008   3.27152   0.514858

733   c/z    53.98008   3.27152   0.602996

734   c/z    55.61584   3.27152   0.514858

735   c/z    55.61584   3.27152   0.602996

736   c/z    57.25160   3.27152   0.514858

737   c/z    57.25160   3.27152   0.602996

738   c/z    58.88736   3.27152   0.514858

739   c/z    58.88736   3.27152   0.602996

740   c/z    60.52312   3.27152   0.514858

741   c/z    60.52312   3.27152   0.602996

742   c/z    62.15888   3.27152   0.514858

743   c/z    62.15888   3.27152   0.602996

744   c/z    63.79464   3.27152   0.514858

745   c/z    63.79464   3.27152   0.602996

746   c/z    65.43040   3.27152   0.514858

747   c/z    65.43040   3.27152   0.602996

748   c/z    37.62248   4.90728   0.514858

749   c/z    37.62248   4.90728   0.602996

750   c/z    39.25824   4.90728   0.514858

751   c/z    39.25824   4.90728   0.602996

752   c/z    40.89400   4.90728   0.514858

753   c/z    40.89400   4.90728   0.602996

754   c/z    42.52976   4.90728   0.514858

755   c/z    42.52976   4.90728   0.602996

756   c/z    44.16552   4.90728   0.514858

757   c/z    44.16552   4.90728   0.602996

758   c/z    45.80128   4.90728   0.514858

759   c/z    45.80128   4.90728   0.602996

760   c/z    47.43704   4.90728   0.514858

761   c/z    47.43704   4.90728   0.602996

762   c/z    49.07280   4.90728   0.514858

763   c/z    49.07280   4.90728   0.602996

764   c/z    50.70856   4.90728   0.514858

765   c/z    50.70856   4.90728   0.602996

766   c/z    52.34432   4.90728   0.514858

767   c/z    52.34432   4.90728   0.602996

768   c/z    53.98008   4.90728   0.514858

769   c/z    53.98008   4.90728   0.602996

770   c/z    55.61584   4.90728   0.514858

771   c/z    55.61584   4.90728   0.602996

772   c/z    57.25160   4.90728   0.514858

773   c/z    57.25160   4.90728   0.602996

774   c/z    58.88736   4.90728   0.514858

775   c/z    58.88736   4.90728   0.602996

776   c/z    60.52312   4.90728   0.514858

777   c/z    60.52312   4.90728   0.602996

778   c/z    62.15888   4.90728   0.514858

779   c/z    62.15888   4.90728   0.602996

780   c/z    63.79464   4.90728   0.514858

781   c/z    63.79464   4.90728   0.602996

782   c/z    65.43040   4.90728   0.514858

783   c/z    65.43040   4.90728   0.602996

784   c/z    37.62248   6.54304   0.514858

785   c/z    37.62248   6.54304   0.602996

786   c/z    39.25824   6.54304   0.514858

787   c/z    39.25824   6.54304   0.602996

788   c/z    40.89400   6.54304   0.514858

789   c/z    40.89400   6.54304   0.602996

790   c/z    42.52976   6.54304   0.514858

791   c/z    42.52976   6.54304   0.602996

792   c/z    44.16552   6.54304   0.514858

793   c/z    44.16552   6.54304   0.602996

794   c/z    45.80128   6.54304   0.514858

795   c/z    45.80128   6.54304   0.602996

796   c/z    47.43704   6.54304   0.514858

797   c/z    47.43704   6.54304   0.602996

798   c/z    49.07280   6.54304   0.514858

799   c/z    49.07280   6.54304   0.602996

800   c/z    50.70856   6.54304   0.514858

801   c/z    50.70856   6.54304   0.602996

802   c/z    52.34432   6.54304   0.514858

803   c/z    52.34432   6.54304   0.602996

804   c/z    53.98008   6.54304   0.514858

805   c/z    53.98008   6.54304   0.602996

806   c/z    55.61584   6.54304   0.514858

807   c/z    55.61584   6.54304   0.602996

808   c/z    57.25160   6.54304   0.514858

809   c/z    57.25160   6.54304   0.602996

810   c/z    58.88736   6.54304   0.514858

811   c/z    58.88736   6.54304   0.602996

812   c/z    60.52312   6.54304   0.514858

813   c/z    60.52312   6.54304   0.602996

814   c/z    62.15888   6.54304   0.514858

815   c/z    62.15888   6.54304   0.602996

816   c/z    63.79464   6.54304   0.514858

817   c/z    63.79464   6.54304   0.602996

818   c/z    65.43040   6.54304   0.514858

819   c/z    65.43040   6.54304   0.602996

820   c/z    37.62248   8.17880   0.514858

821   c/z    37.62248   8.17880   0.602996

822   c/z    39.25824   8.17880   0.514858

823   c/z    39.25824   8.17880   0.602996

824   c/z    40.89400   8.17880   0.514858

825   c/z    40.89400   8.17880   0.602996

826   c/z    42.52976   8.17880   0.514858

827   c/z    42.52976   8.17880   0.602996

828   c/z    44.16552   8.17880   0.514858

829   c/z    44.16552   8.17880   0.602996

830   c/z    45.80128   8.17880   0.514858

831   c/z    45.80128   8.17880   0.602996

832   c/z    47.43704   8.17880   0.514858

833   c/z    47.43704   8.17880   0.602996

834   c/z    49.07280   8.17880   0.514858

835   c/z    49.07280   8.17880   0.602996

836   c/z    50.70856   8.17880   0.514858

837   c/z    50.70856   8.17880   0.602996

838   c/z    52.34432   8.17880   0.514858

839   c/z    52.34432   8.17880   0.602996

840   c/z    53.98008   8.17880   0.514858

841   c/z    53.98008   8.17880   0.602996

842   c/z    55.61584   8.17880   0.514858

843   c/z    55.61584   8.17880   0.602996

844   c/z    57.25160   8.17880   0.514858

845   c/z    57.25160   8.17880   0.602996

846   c/z    58.88736   8.17880   0.514858

847   c/z    58.88736   8.17880   0.602996

848   c/z    60.52312   8.17880   0.514858

849   c/z    60.52312   8.17880   0.602996

850   c/z    62.15888   8.17880   0.514858

851   c/z    62.15888   8.17880   0.602996

852   c/z    63.79464   8.17880   0.514858

853   c/z    63.79464   8.17880   0.602996

854   c/z    65.43040   8.17880   0.514858

855   c/z    65.43040   8.17880   0.602996

856   c/z    37.62248   9.81456   0.514858

857   c/z    37.62248   9.81456   0.602996

858   c/z    39.25824   9.81456   0.514858

859   c/z    39.25824   9.81456   0.602996

860   c/z    40.89400   9.81456   0.514858

861   c/z    40.89400   9.81456   0.602996

862   c/z    42.52976   9.81456   0.514858

863   c/z    42.52976   9.81456   0.602996

864   c/z    44.16552   9.81456   0.514858

865   c/z    44.16552   9.81456   0.602996

866   c/z    45.80128   9.81456   0.514858

867   c/z    45.80128   9.81456   0.602996

868   c/z    47.43704   9.81456   0.514858

869   c/z    47.43704   9.81456   0.602996

870   c/z    49.07280   9.81456   0.514858

871   c/z    49.07280   9.81456   0.602996

872   c/z    50.70856   9.81456   0.514858

873   c/z    50.70856   9.81456   0.602996

874   c/z    52.34432   9.81456   0.514858

875   c/z    52.34432   9.81456   0.602996

876   c/z    53.98008   9.81456   0.514858

877   c/z    53.98008   9.81456   0.602996

878   c/z    55.61584   9.81456   0.514858

879   c/z    55.61584   9.81456   0.602996

880   c/z    57.25160   9.81456   0.514858

881   c/z    57.25160   9.81456   0.602996

882   c/z    58.88736   9.81456   0.514858

883   c/z    58.88736   9.81456   0.602996

884   c/z    60.52312   9.81456   0.514858

885   c/z    60.52312   9.81456   0.602996

886   c/z    62.15888   9.81456   0.514858

887   c/z    62.15888   9.81456   0.602996

888   c/z    63.79464   9.81456   0.514858

889   c/z    63.79464   9.81456   0.602996

890   c/z    65.43040   9.81456   0.514858

891   c/z    65.43040   9.81456   0.602996

892   c/z    37.62248  11.45032   0.514858

893   c/z    37.62248  11.45032   0.602996

894   c/z    39.25824  11.45032   0.514858

895   c/z    39.25824  11.45032   0.602996

896   c/z    40.89400  11.45032   0.514858

897   c/z    40.89400  11.45032   0.602996

898   c/z    42.52976  11.45032   0.514858

899   c/z    42.52976  11.45032   0.602996

900   c/z    44.16552  11.45032   0.514858

901   c/z    44.16552  11.45032   0.602996

902   c/z    45.80128  11.45032   0.514858

903   c/z    45.80128  11.45032   0.602996

904   c/z    47.43704  11.45032   0.514858

905   c/z    47.43704  11.45032   0.602996

906   c/z    49.07280  11.45032   0.514858

907   c/z    49.07280  11.45032   0.602996

908   c/z    50.70856  11.45032   0.514858

909   c/z    50.70856  11.45032   0.602996

910   c/z    52.34432  11.45032   0.514858

911   c/z    52.34432  11.45032   0.602996

912   c/z    53.98008  11.45032   0.514858

913   c/z    53.98008  11.45032   0.602996

914   c/z    55.61584  11.45032   0.514858

915   c/z    55.61584  11.45032   0.602996

916   c/z    57.25160  11.45032   0.514858

917   c/z    57.25160  11.45032   0.602996

918   c/z    58.88736  11.45032   0.514858

919   c/z    58.88736  11.45032   0.602996

920   c/z    60.52312  11.45032   0.514858

921   c/z    60.52312  11.45032   0.602996

922   c/z    62.15888  11.45032   0.514858

923   c/z    62.15888  11.45032   0.602996

924   c/z    63.79464  11.45032   0.514858

925   c/z    63.79464  11.45032   0.602996

926   c/z    65.43040  11.45032   0.514858

927   c/z    65.43040  11.45032   0.602996

928   c/z    37.62248  13.08608   0.514858

929   c/z    37.62248  13.08608   0.602996

930   c/z    39.25824  13.08608   0.514858

931   c/z    39.25824  13.08608   0.602996

932   c/z    40.89400  13.08608   0.514858

933   c/z    40.89400  13.08608   0.602996

934   c/z    42.52976  13.08608   0.514858

935   c/z    42.52976  13.08608   0.602996

936   c/z    44.16552  13.08608   0.514858

937   c/z    44.16552  13.08608   0.602996

938   c/z    45.80128  13.08608   0.514858

939   c/z    45.80128  13.08608   0.602996

940   c/z    47.43704  13.08608   0.514858

941   c/z    47.43704  13.08608   0.602996

942   c/z    49.07280  13.08608   0.514858

943   c/z    49.07280  13.08608   0.602996

944   c/z    50.70856  13.08608   0.514858

945   c/z    50.70856  13.08608   0.602996

946   c/z    52.34432  13.08608   0.514858

947   c/z    52.34432  13.08608   0.602996

948   c/z    53.98008  13.08608   0.514858

949   c/z    53.98008  13.08608   0.602996

950   c/z    55.61584  13.08608   0.514858

951   c/z    55.61584  13.08608   0.602996

952   c/z    57.25160  13.08608   0.514858

953   c/z    57.25160  13.08608   0.602996

954   c/z    58.88736  13.08608   0.514858

955   c/z    58.88736  13.08608   0.602996

956   c/z    60.52312  13.08608   0.514858

957   c/z    60.52312  13.08608   0.602996

958   c/z    62.15888  13.08608   0.514858

959   c/z    62.15888  13.08608   0.602996

960   c/z    63.79464  13.08608   0.514858

961   c/z    63.79464  13.08608   0.602996

962   c/z    65.43040  13.08608   0.514858

963   c/z    65.43040  13.08608   0.602996

964   c/z    37.62248  14.72184   0.514858

965   c/z    37.62248  14.72184   0.602996

966   c/z    39.25824  14.72184   0.514858

967   c/z    39.25824  14.72184   0.602996

968   c/z    40.89400  14.72184   0.514858

969   c/z    40.89400  14.72184   0.602996

970   c/z    42.52976  14.72184   0.514858

971   c/z    42.52976  14.72184   0.602996

972   c/z    44.16552  14.72184   0.514858

973   c/z    44.16552  14.72184   0.602996

974   c/z    45.80128  14.72184   0.514858

975   c/z    45.80128  14.72184   0.602996

976   c/z    47.43704  14.72184   0.514858

977   c/z    47.43704  14.72184   0.602996

978   c/z    49.07280  14.72184   0.514858

979   c/z    49.07280  14.72184   0.602996

980   c/z    50.70856  14.72184   0.514858

981   c/z    50.70856  14.72184   0.602996

982   c/z    52.34432  14.72184   0.514858

983   c/z    52.34432  14.72184   0.602996

984   c/z    53.98008  14.72184   0.514858

985   c/z    53.98008  14.72184   0.602996

986   c/z    55.61584  14.72184   0.514858

987   c/z    55.61584  14.72184   0.602996

988   c/z    57.25160  14.72184   0.514858

989   c/z    57.25160  14.72184   0.602996

990   c/z    58.88736  14.72184   0.514858

991   c/z    58.88736  14.72184   0.602996

992   c/z    60.52312  14.72184   0.514858

993   c/z    60.52312  14.72184   0.602996

994   c/z    62.15888  14.72184   0.514858

995   c/z    62.15888  14.72184   0.602996

996   c/z    63.79464  14.72184   0.514858

997   c/z    63.79464  14.72184   0.602996

998   c/z    65.43040  14.72184   0.514858

999   c/z    65.43040  14.72184   0.602996

1000  c/z    37.62248  16.35760   0.514858

1001  c/z    37.62248  16.35760   0.602996

1002  c/z    39.25824  16.35760   0.514858

1003  c/z    39.25824  16.35760   0.602996

1004  c/z    40.89400  16.35760   0.514858

1005  c/z    40.89400  16.35760   0.602996

1006  c/z    42.52976  16.35760   0.514858

1007  c/z    42.52976  16.35760   0.602996

1008  c/z    44.16552  16.35760   0.514858

1009  c/z    44.16552  16.35760   0.602996

1010  c/z    45.80128  16.35760   0.514858

1011  c/z    45.80128  16.35760   0.602996

1012  c/z    47.43704  16.35760   0.514858

1013  c/z    47.43704  16.35760   0.602996

1014  c/z    49.07280  16.35760   0.514858

1015  c/z    49.07280  16.35760   0.602996

1016  c/z    50.70856  16.35760   0.514858

1017  c/z    50.70856  16.35760   0.602996

1018  c/z    52.34432  16.35760   0.514858

1019  c/z    52.34432  16.35760   0.602996

1020  c/z    53.98008  16.35760   0.514858

1021  c/z    53.98008  16.35760   0.602996

1022  c/z    55.61584  16.35760   0.514858

1023  c/z    55.61584  16.35760   0.602996

1024  c/z    57.25160  16.35760   0.514858

1025  c/z    57.25160  16.35760   0.602996

1026  c/z    58.88736  16.35760   0.514858

1027  c/z    58.88736  16.35760   0.602996

1028  c/z    60.52312  16.35760   0.514858

1029  c/z    60.52312  16.35760   0.602996

1030  c/z    62.15888  16.35760   0.514858

1031  c/z    62.15888  16.35760   0.602996

1032  c/z    63.79464  16.35760   0.514858

1033  c/z    63.79464  16.35760   0.602996

1034  c/z    65.43040  16.35760   0.514858

1035  c/z    65.43040  16.35760   0.602996

1036  c/z    37.62248  17.99336   0.514858

1037  c/z    37.62248  17.99336   0.602996

1038  c/z    39.25824  17.99336   0.514858

1039  c/z    39.25824  17.99336   0.602996

1040  c/z    40.89400  17.99336   0.514858

1041  c/z    40.89400  17.99336   0.602996

1042  c/z    42.52976  17.99336   0.514858

1043  c/z    42.52976  17.99336   0.602996

1044  c/z    44.16552  17.99336   0.514858

1045  c/z    44.16552  17.99336   0.602996

1046  c/z    45.80128  17.99336   0.514858

1047  c/z    45.80128  17.99336   0.602996

1048  c/z    47.43704  17.99336   0.514858

1049  c/z    47.43704  17.99336   0.602996

1050  c/z    49.07280  17.99336   0.514858

1051  c/z    49.07280  17.99336   0.602996

1052  c/z    50.70856  17.99336   0.514858

1053  c/z    50.70856  17.99336   0.602996

1054  c/z    52.34432  17.99336   0.514858

1055  c/z    52.34432  17.99336   0.602996

1056  c/z    53.98008  17.99336   0.514858

1057  c/z    53.98008  17.99336   0.602996

1058  c/z    55.61584  17.99336   0.514858

1059  c/z    55.61584  17.99336   0.602996

1060  c/z    57.25160  17.99336   0.514858

1061  c/z    57.25160  17.99336   0.602996

1062  c/z    37.62248  19.62912   0.514858

1063  c/z    37.62248  19.62912   0.602996

1064  c/z    39.25824  19.62912   0.514858

1065  c/z    39.25824  19.62912   0.602996

1066  c/z    40.89400  19.62912   0.514858

1067  c/z    40.89400  19.62912   0.602996

1068  c/z    42.52976  19.62912   0.514858

1069  c/z    42.52976  19.62912   0.602996

1070  c/z    44.16552  19.62912   0.514858

1071  c/z    44.16552  19.62912   0.602996

1072  c/z    45.80128  19.62912   0.514858

1073  c/z    45.80128  19.62912   0.602996

1074  c/z    47.43704  19.62912   0.514858

1075  c/z    47.43704  19.62912   0.602996

1076  c/z    49.07280  19.62912   0.514858

1077  c/z    49.07280  19.62912   0.602996

1078  c/z    50.70856  19.62912   0.514858

1079  c/z    50.70856  19.62912   0.602996

1080  c/z    52.34432  19.62912   0.514858

1081  c/z    52.34432  19.62912   0.602996

1082  c/z    53.98008  19.62912   0.514858

1083  c/z    53.98008  19.62912   0.602996

1084  c/z    55.61584  19.62912   0.514858

1085  c/z    55.61584  19.62912   0.602996

1086  c/z    57.25160  19.62912   0.514858

1087  c/z    57.25160  19.62912   0.602996

1088  c/z    37.62248  21.26488   0.514858

1089  c/z    37.62248  21.26488   0.602996

1090  c/z    39.25824  21.26488   0.514858

1091  c/z    39.25824  21.26488   0.602996

1092  c/z    40.89400  21.26488   0.514858

1093  c/z    40.89400  21.26488   0.602996

1094  c/z    42.52976  21.26488   0.514858

1095  c/z    42.52976  21.26488   0.602996

1096  c/z    44.16552  21.26488   0.514858

1097  c/z    44.16552  21.26488   0.602996

1098  c/z    45.80128  21.26488   0.514858

1099  c/z    45.80128  21.26488   0.602996

1100  c/z    47.43704  21.26488   0.514858

1101  c/z    47.43704  21.26488   0.602996

1102  c/z    49.07280  21.26488   0.514858

1103  c/z    49.07280  21.26488   0.602996

1104  c/z    50.70856  21.26488   0.514858

1105  c/z    50.70856  21.26488   0.602996

1106  c/z    52.34432  21.26488   0.514858

1107  c/z    52.34432  21.26488   0.602996

1108  c/z    53.98008  21.26488   0.514858

1109  c/z    53.98008  21.26488   0.602996

1110  c/z    55.61584  21.26488   0.514858

1111  c/z    55.61584  21.26488   0.602996

1112  c/z    57.25160  21.26488   0.514858

1113  c/z    57.25160  21.26488   0.602996

1114  c/z    37.62248  22.90064   0.514858

1115  c/z    37.62248  22.90064   0.602996

1116  c/z    39.25824  22.90064   0.514858

1117  c/z    39.25824  22.90064   0.602996

1118  c/z    40.89400  22.90064   0.514858

1119  c/z    40.89400  22.90064   0.602996

1120  c/z    42.52976  22.90064   0.514858

1121  c/z    42.52976  22.90064   0.602996

1122  c/z    44.16552  22.90064   0.514858

1123  c/z    44.16552  22.90064   0.602996

1124  c/z    45.80128  22.90064   0.514858

1125  c/z    45.80128  22.90064   0.602996

1126  c/z    47.43704  22.90064   0.514858

1127  c/z    47.43704  22.90064   0.602996

1128  c/z    49.07280  22.90064   0.514858

1129  c/z    49.07280  22.90064   0.602996

1130  c/z    50.70856  22.90064   0.514858

1131  c/z    50.70856  22.90064   0.602996

1132  c/z    52.34432  22.90064   0.514858

1133  c/z    52.34432  22.90064   0.602996

1134  c/z    53.98008  22.90064   0.514858

1135  c/z    53.98008  22.90064   0.602996

1136  c/z    55.61584  22.90064   0.514858

1137  c/z    55.61584  22.90064   0.602996

1138  c/z    57.25160  22.90064   0.514858

1139  c/z    57.25160  22.90064   0.602996

1140  c/z    37.62248  24.53640   0.514858

1141  c/z    37.62248  24.53640   0.602996

1142  c/z    39.25824  24.53640   0.514858

1143  c/z    39.25824  24.53640   0.602996

1144  c/z    40.89400  24.53640   0.514858

1145  c/z    40.89400  24.53640   0.602996

1146  c/z    42.52976  24.53640   0.514858

1147  c/z    42.52976  24.53640   0.602996

1148  c/z    44.16552  24.53640   0.514858

1149  c/z    44.16552  24.53640   0.602996

1150  c/z    45.80128  24.53640   0.514858

1151  c/z    45.80128  24.53640   0.602996

1152  c/z    47.43704  24.53640   0.514858

1153  c/z    47.43704  24.53640   0.602996

1154  c/z    49.07280  24.53640   0.514858

1155  c/z    49.07280  24.53640   0.602996

1156  c/z    50.70856  24.53640   0.514858

1157  c/z    50.70856  24.53640   0.602996

1158  c/z    52.34432  24.53640   0.514858

1159  c/z    52.34432  24.53640   0.602996

1160  c/z    53.98008  24.53640   0.514858

1161  c/z    53.98008  24.53640   0.602996

1162  c/z    55.61584  24.53640   0.514858

1163  c/z    55.61584  24.53640   0.602996

1164  c/z    57.25160  24.53640   0.514858

1165  c/z    57.25160  24.53640   0.602996

1166  c/z    37.62248  26.17216   0.514858

1167  c/z    37.62248  26.17216   0.602996

1168  c/z    39.25824  26.17216   0.514858

1169  c/z    39.25824  26.17216   0.602996

1170  c/z    40.89400  26.17216   0.514858

1171  c/z    40.89400  26.17216   0.602996

1172  c/z    42.52976  26.17216   0.514858

1173  c/z    42.52976  26.17216   0.602996

1174  c/z    44.16552  26.17216   0.514858

1175  c/z    44.16552  26.17216   0.602996

1176  c/z    45.80128  26.17216   0.514858

1177  c/z    45.80128  26.17216   0.602996

1178  c/z    47.43704  26.17216   0.514858

1179  c/z    47.43704  26.17216   0.602996

1180  c/z    49.07280  26.17216   0.514858

1181  c/z    49.07280  26.17216   0.602996

1182  c/z    50.70856  26.17216   0.514858

1183  c/z    50.70856  26.17216   0.602996

1184  c/z    52.34432  26.17216   0.514858

1185  c/z    52.34432  26.17216   0.602996

1186  c/z    53.98008  26.17216   0.514858

1187  c/z    53.98008  26.17216   0.602996

1188  c/z    55.61584  26.17216   0.514858

1189  c/z    55.61584  26.17216   0.602996

1190  c/z    57.25160  26.17216   0.514858

1191  c/z    57.25160  26.17216   0.602996

1192  c/z    37.62248  27.80792   0.514858

1193  c/z    37.62248  27.80792   0.602996

1194  c/z    39.25824  27.80792   0.514858

1195  c/z    39.25824  27.80792   0.602996

1196  c/z    40.89400  27.80792   0.514858

1197  c/z    40.89400  27.80792   0.602996

1198  c/z    42.52976  27.80792   0.514858

1199  c/z    42.52976  27.80792   0.602996

1200  c/z    44.16552  27.80792   0.514858

1201  c/z    44.16552  27.80792   0.602996

1202  c/z    45.80128  27.80792   0.514858

1203  c/z    45.80128  27.80792   0.602996

1204  c/z    47.43704  27.80792   0.514858

1205  c/z    47.43704  27.80792   0.602996

1206  c/z    49.07280  27.80792   0.514858

1207  c/z    49.07280  27.80792   0.602996

1208  c/z    50.70856  27.80792   0.514858

1209  c/z    50.70856  27.80792   0.602996

1210  c/z    52.34432  27.80792   0.514858

1211  c/z    52.34432  27.80792   0.602996

1212  c/z    53.98008  27.80792   0.514858

1213  c/z    53.98008  27.80792   0.602996

1214  c/z    55.61584  27.80792   0.514858

1215  c/z    55.61584  27.80792   0.602996

1216  c/z    57.25160  27.80792   0.514858

1217  c/z    57.25160  27.80792   0.602996

1218  c/z    37.62248  29.44368   0.514858

1219  c/z    37.62248  29.44368   0.602996

1220  c/z    39.25824  29.44368   0.514858

1221  c/z    39.25824  29.44368   0.602996

1222  c/z    40.89400  29.44368   0.514858

1223  c/z    40.89400  29.44368   0.602996

1224  c/z    42.52976  29.44368   0.514858

1225  c/z    42.52976  29.44368   0.602996

1226  c/z    44.16552  29.44368   0.514858

1227  c/z    44.16552  29.44368   0.602996

1228  c/z    45.80128  29.44368   0.514858

1229  c/z    45.80128  29.44368   0.602996

1230  c/z    47.43704  29.44368   0.514858

1231  c/z    47.43704  29.44368   0.602996

1232  c/z    49.07280  29.44368   0.514858

1233  c/z    49.07280  29.44368   0.602996

1234  c/z    50.70856  29.44368   0.514858

1235  c/z    50.70856  29.44368   0.602996

1236  c/z    52.34432  29.44368   0.514858

1237  c/z    52.34432  29.44368   0.602996

1238  c/z    53.98008  29.44368   0.514858

1239  c/z    53.98008  29.44368   0.602996

1240  c/z    55.61584  29.44368   0.514858

1241  c/z    55.61584  29.44368   0.602996

1242  c/z    57.25160  29.44368   0.514858

1243  c/z    57.25160  29.44368   0.602996

1244  c/z    37.62248  31.07944   0.514858

1245  c/z    37.62248  31.07944   0.602996

1246  c/z    39.25824  31.07944   0.514858

1247  c/z    39.25824  31.07944   0.602996

1248  c/z    40.89400  31.07944   0.514858

1249  c/z    40.89400  31.07944   0.602996

1250  c/z    42.52976  31.07944   0.514858

1251  c/z    42.52976  31.07944   0.602996

1252  c/z    44.16552  31.07944   0.514858

1253  c/z    44.16552  31.07944   0.602996

1254  c/z    45.80128  31.07944   0.514858

1255  c/z    45.80128  31.07944   0.602996

1256  c/z    47.43704  31.07944   0.514858

1257  c/z    47.43704  31.07944   0.602996

1258  c/z    49.07280  31.07944   0.514858

1259  c/z    49.07280  31.07944   0.602996

1260  c/z    50.70856  31.07944   0.514858

1261  c/z    50.70856  31.07944   0.602996

1262  c/z    52.34432  31.07944   0.514858

1263  c/z    52.34432  31.07944   0.602996

1264  c/z    53.98008  31.07944   0.514858

1265  c/z    53.98008  31.07944   0.602996

1266  c/z    55.61584  31.07944   0.514858

1267  c/z    55.61584  31.07944   0.602996

1268  c/z    57.25160  31.07944   0.514858

1269  c/z    57.25160  31.07944   0.602996

1270  c/z    37.62248  32.71520   0.514858

1271  c/z    37.62248  32.71520   0.602996

1272  c/z    39.25824  32.71520   0.514858

1273  c/z    39.25824  32.71520   0.602996

1274  c/z    40.89400  32.71520   0.514858

1275  c/z    40.89400  32.71520   0.602996

1276  c/z    42.52976  32.71520   0.514858

1277  c/z    42.52976  32.71520   0.602996

1278  c/z    44.16552  32.71520   0.514858

1279  c/z    44.16552  32.71520   0.602996

1280  c/z    45.80128  32.71520   0.514858

1281  c/z    45.80128  32.71520   0.602996

1282  c/z    47.43704  32.71520   0.514858

1283  c/z    47.43704  32.71520   0.602996

1284  c/z    49.07280  32.71520   0.514858

1285  c/z    49.07280  32.71520   0.602996

1286  c/z    50.70856  32.71520   0.514858

1287  c/z    50.70856  32.71520   0.602996

1288  c/z    52.34432  32.71520   0.514858

1289  c/z    52.34432  32.71520   0.602996

1290  c/z    53.98008  32.71520   0.514858

1291  c/z    53.98008  32.71520   0.602996

1292  c/z    55.61584  32.71520   0.514858

1293  c/z    55.61584  32.71520   0.602996

1294  c/z    57.25160  32.71520   0.514858

1295  c/z    57.25160  32.71520   0.602996

1296  c/z    37.62248  34.35096   0.514858

1297  c/z    37.62248  34.35096   0.602996

1298  c/z    39.25824  34.35096   0.514858

1299  c/z    39.25824  34.35096   0.602996

1300  c/z    40.89400  34.35096   0.514858

1301  c/z    40.89400  34.35096   0.602996

1302  c/z    42.52976  34.35096   0.514858

1303  c/z    42.52976  34.35096   0.602996

1304  c/z    44.16552  34.35096   0.514858

1305  c/z    44.16552  34.35096   0.602996

1306  c/z    45.80128  34.35096   0.514858

1307  c/z    45.80128  34.35096   0.602996

1308  c/z    47.43704  34.35096   0.514858

1309  c/z    47.43704  34.35096   0.602996

1310  c/z    49.07280  34.35096   0.514858

1311  c/z    49.07280  34.35096   0.602996

1312  c/z    37.62248  35.98672   0.514858

1313  c/z    37.62248  35.98672   0.602996

1314  c/z    39.25824  35.98672   0.514858

1315  c/z    39.25824  35.98672   0.602996

1316  c/z    40.89400  35.98672   0.514858

1317  c/z    40.89400  35.98672   0.602996

1318  c/z    42.52976  35.98672   0.514858

1319  c/z    42.52976  35.98672   0.602996

1320  c/z    44.16552  35.98672   0.514858

1321  c/z    44.16552  35.98672   0.602996

1322  c/z    45.80128  35.98672   0.514858

1323  c/z    45.80128  35.98672   0.602996

1324  c/z    47.43704  35.98672   0.514858

1325  c/z    47.43704  35.98672   0.602996

1326  c/z    49.07280  35.98672   0.514858

1327  c/z    49.07280  35.98672   0.602996

1328  c/z    37.62248  37.62248   0.514858

1329  c/z    37.62248  37.62248   0.602996

1330  c/z    39.25824  37.62248   0.514858

1331  c/z    39.25824  37.62248   0.602996

1332  c/z    40.89400  37.62248   0.514858

1333  c/z    40.89400  37.62248   0.602996

1334  c/z    42.52976  37.62248   0.514858

1335  c/z    42.52976  37.62248   0.602996

1336  c/z    44.16552  37.62248   0.514858

1337  c/z    44.16552  37.62248   0.602996

1338  c/z    45.80128  37.62248   0.514858

1339  c/z    45.80128  37.62248   0.602996

1340  c/z    47.43704  37.62248   0.514858

1341  c/z    47.43704  37.62248   0.602996

1342  c/z    49.07280  37.62248   0.514858

1343  c/z    49.07280  37.62248   0.602996

1344  c/z    39.25824  39.25824   0.514858

1345  c/z    39.25824  39.25824   0.602996

1346  c/z    40.89400  39.25824   0.514858

1347  c/z    40.89400  39.25824   0.602996

1348  c/z    42.52976  39.25824   0.514858

1349  c/z    42.52976  39.25824   0.602996

1350  c/z    44.16552  39.25824   0.514858

1351  c/z    44.16552  39.25824   0.602996

1352  c/z    45.80128  39.25824   0.514858

1353  c/z    45.80128  39.25824   0.602996

1354  c/z    47.43704  39.25824   0.514858

1355  c/z    47.43704  39.25824   0.602996

1356  c/z    49.07280  39.25824   0.514858

1357  c/z    49.07280  39.25824   0.602996

1358  c/z    40.89400  40.89400   0.514858

1359  c/z    40.89400  40.89400   0.602996

1360  c/z    42.52976  40.89400   0.514858

1361  c/z    42.52976  40.89400   0.602996

1362  c/z    44.16552  40.89400   0.514858

1363  c/z    44.16552  40.89400   0.602996

1364  c/z    45.80128  40.89400   0.514858

1365  c/z    45.80128  40.89400   0.602996

1366  c/z    47.43704  40.89400   0.514858

1367  c/z    47.43704  40.89400   0.602996

1368  c/z    49.07280  40.89400   0.514858

1369  c/z    49.07280  40.89400   0.602996

1370  c/z    42.52976  42.52976   0.514858

1371  c/z    42.52976  42.52976   0.602996

1372  c/z    44.16552  42.52976   0.514858

1373  c/z    44.16552  42.52976   0.602996

1374  c/z    45.80128  42.52976   0.514858

1375  c/z    45.80128  42.52976   0.602996

1376  c/z    47.43704  42.52976   0.514858

1377  c/z    47.43704  42.52976   0.602996

1378  c/z    49.07280  42.52976   0.514858

1379  c/z    49.07280  42.52976   0.602996

1380  c/z    44.16552  44.16552   0.514858

1381  c/z    44.16552  44.16552   0.602996

1382  c/z    45.80128  44.16552   0.514858

1383  c/z    45.80128  44.16552   0.602996

1384  c/z    47.43704  44.16552   0.514858

1385  c/z    47.43704  44.16552   0.602996

1386  c/z    49.07280  44.16552   0.514858

1387  c/z    49.07280  44.16552   0.602996

1388  c/z    45.80128  45.80128   0.514858

1389  c/z    45.80128  45.80128   0.602996

1390  c/z    47.43704  45.80128   0.514858

1391  c/z    47.43704  45.80128   0.602996

1392  c/z    49.07280  45.80128   0.514858

1393  c/z    49.07280  45.80128   0.602996

1394  c/z    47.43704  47.43704   0.514858

1395  c/z    47.43704  47.43704   0.602996

1396  c/z    49.07280  47.43704   0.514858

1397  c/z    49.07280  47.43704   0.602996

1398  c/z    49.07280  49.07280   0.514858

1399  c/z    49.07280  49.07280   0.602996

mode      n

kcode     5000     1.0     200     1200

imp:n     1.0    2001r    0.0

f4:n        4   7  10  13  16  19  22  25  28  31  34  37  40  43  49

52  58  61  64  67  70  73  76  82  85  88  91  94  97 100

103 106   t

fm4       0.068525  1  -6

vol        17.001    6.319   31.306    68.006   25.277  125.222

68.006   25.277  125.222    68.006   25.277  125.222

68.006   25.277  125.222    68.006   25.277  125.222

68.006   25.277  125.222    68.006   25.277  125.222

68.006   25.277  125.222   136.011   50.553  250.444

136.011   50.553  250.444   136.011   50.553  250.444

136.011   50.553  250.444   136.011   50.553  250.444

136.011   50.553  250.444    68.006   25.277  125.222

136.011   50.553  250.444   136.011   50.553  250.444

136.011   50.553  250.444   136.011   50.553  250.444

136.011   50.553  250.444    68.006   25.277  125.222

136.011   50.553  250.444   136.011   50.553  250.444

136.011   50.553  250.444   136.011   50.553  250.444

68.006   25.277  125.222   136.011   50.553  250.444

136.011   50.553  250.444   136.011   50.553  250.444

68.006   25.277  125.222   136.011   50.553  250.444

136.011   50.553  250.444    68.006   25.277  125.222

136.011   50.553  250.444    68.006   25.277  125.222

1.0     1893r     0.0

ksrc      0.0001   0.0001  -70.0     1.63576  0.0001  -70.0

3.27152  0.0001  -70.0     4.90728  0.0001  -70.0

6.54304  0.0001  -70.0     8.17880  0.0001  -70.0

9.81456  0.0001  -70.0    11.45032  0.0001  -70.0

13.08608  0.0001  -70.0    14.72184  0.0001  -70.0

16.35760  0.0001  -70.0    17.99336  0.0001  -70.0

19.62912  0.0001  -70.0    21.26488  0.0001  -70.0

22.90064  0.0001  -70.0    24.53640  0.0001  -70.0

26.17216  0.0001  -70.0    27.80792  0.0001  -70.0

29.44368  0.0001  -70.0    31.07944  0.0001  -70.0

32.71520  0.0001  -70.0    34.35096  0.0001  -70.0

35.98672  0.0001  -70.0    37.62248  0.0001  -70.0

39.25824  0.0001  -70.0    40.89400  0.0001  -70.0

42.52976  0.0001  -70.0    44.16552  0.0001  -70.0

45.80128  0.0001  -70.0    47.43704  0.0001  -70.0

49.07280  0.0001  -70.0

0.0001   0.0001    0.0     1.63576  0.0001    0.0

3.27152  0.0001    0.0     4.90728  0.0001    0.0

6.54304  0.0001    0.0     8.17880  0.0001    0.0

9.81456  0.0001    0.0    11.45032  0.0001    0.0

13.08608  0.0001    0.0    14.72184  0.0001    0.0

16.35760  0.0001    0.0    17.99336  0.0001    0.0

19.62912  0.0001    0.0    21.26488  0.0001    0.0

22.90064  0.0001    0.0    24.53640  0.0001    0.0

26.17216  0.0001    0.0    27.80792  0.0001    0.0

29.44368  0.0001    0.0    31.07944  0.0001    0.0

32.71520  0.0001    0.0    34.35096  0.0001    0.0

35.98672  0.0001    0.0    37.62248  0.0001    0.0

39.25824  0.0001    0.0    40.89400  0.0001    0.0

42.52976  0.0001    0.0    44.16552  0.0001    0.0

45.80128  0.0001    0.0    47.43704  0.0001    0.0

49.07280  0.0001    0.0

0.0001   0.0001   70.0     1.63576  0.0001   70.0

3.27152  0.0001   70.0     4.90728  0.0001   70.0

6.54304  0.0001   70.0     8.17880  0.0001   70.0

9.81456  0.0001   70.0    11.45032  0.0001   70.0

13.08608  0.0001   70.0    14.72184  0.0001   70.0

16.35760  0.0001   70.0    17.99336  0.0001   70.0

19.62912  0.0001   70.0    21.26488  0.0001   70.0

22.90064  0.0001   70.0    24.53640  0.0001   70.0

26.17216  0.0001   70.0    27.80792  0.0001   70.0

29.44368  0.0001   70.0    31.07944  0.0001   70.0

32.71520  0.0001   70.0    34.35096  0.0001   70.0

35.98672  0.0001   70.0    37.62248  0.0001   70.0

39.25824  0.0001   70.0    40.89400  0.0001   70.0

42.52976  0.0001   70.0    44.16552  0.0001   70.0

45.80128  0.0001   70.0    47.43704  0.0001   70.0

49.07280  0.0001   70.0

1.63576  1.63500 -70.0     3.27152  3.27100 -70.0

4.90728  4.90700 -70.0     6.54304  6.54200 -70.0

8.17880  8.17800 -70.0     9.81456  9.81400 -70.0

11.45032 11.45000 -70.0    13.08608 13.08500 -70.0

14.72184 14.72100 -70.0    16.35760 16.35700 -70.0

17.99336 17.99300 -70.0    19.62912 19.62800 -70.0

21.26488 21.26400 -70.0    22.90064 22.90000 -70.0

24.53640 24.53600 -70.0    26.17216 26.17200 -70.0

27.80792 27.80700 -70.0    29.44368 29.44300 -70.0

31.07944 31.07900 -70.0    32.71520 32.71500 -70.0

34.35096 34.35000 -70.0    35.98672 35.98600 -70.0

37.62248 37.62200 -70.0    39.25824 39.25800 -70.0

40.89400 40.89390 -70.0    42.52976 42.52900 -70.0

44.16552 44.16500 -70.0    45.80128 45.80100 -70.0

47.43704 47.43600 -70.0    49.07280 49.07200 -70.0

1.63576  1.63500   0.0     3.27152  3.27100   0.0

4.90728  4.90700   0.0     6.54304  6.54200   0.0

8.17880  8.17800   0.0     9.81456  9.81400   0.0

11.45032 11.45000   0.0    13.08608 13.08500   0.0

14.72184 14.72100   0.0    16.35760 16.35700   0.0

17.99336 17.99300   0.0    19.62912 19.62900   0.0

21.26488 21.26400   0.0    22.90064 22.90000   0.0

24.53640 24.53600   0.0    26.17216 26.17200   0.0

27.80792 27.80700   0.0    29.44368 29.44300   0.0

31.07944 31.07900   0.0    32.71520 32.71500   0.0

34.35096 34.35000   0.0    35.98672 35.98600   0.0

37.62248 37.62200   0.0    39.25824 39.25800   0.0

40.89400 40.89300   0.0    42.52976 42.52900   0.0

44.16552 44.16500   0.0    45.80128 45.80100   0.0

47.43704 47.43600   0.0    49.07280 49.07200   0.0

1.63576  1.63500  70.0     3.27152  3.27100  70.0

4.90728  4.90700  70.0     6.54304  6.54200  70.0

8.17880  8.17800  70.0     9.81456  9.81400  70.0

11.45032 11.45000  70.0    13.08608 13.08500  70.0

14.72184 14.72100  70.0    16.35760 16.35700  70.0

17.99336 17.99300  70.0    19.62912 19.62900  70.0

21.26488 21.26400  70.0    22.90064 22.90000  70.0

24.53640 24.53600  70.0    26.17216 26.17200  70.0

27.80792 27.80700  70.0    29.44368 29.44300  70.0

31.07944 31.07900  70.0    32.71520 32.71500  70.0

34.35096 34.35000  70.0    35.98672 35.98600  70.0

37.62248 37.62200  70.0    39.25824 39.25800  70.0

40.89400 40.89300  70.0    42.52976 42.52900  70.0

44.16552 44.16500  70.0    45.80128 45.80100  70.0

47.43704 47.43600  70.0    49.07280 49.07200  70.0

c         Fuel (2.459 w/o with B-10 for impurities)

m1       5010.31c  2.6055E-07

8016.31c  4.5683E-02

92234.31c  4.5689E-06

92235.31c  5.6868E-04

92238.31c  2.2268E-02

c         Aluminum 6061 cladding

m2    12024.31c   4.90307E-04

12025.31c   6.20720E-05

12026.31c   6.83413E-05

13027.31c  5.3985E-02

14028.31c   2.97257E-04

14029.31c   1.50514E-05

14030.31c   9.99130E-06

22046.31c   3.89920E-06

22047.31c   3.51637E-06

22048.31c   3.48423E-05

22049.31c   2.55693E-06

22050.31c   2.44822E-06

24050.31c  2.5214E-06

24052.31c  4.8622E-05

24053.31c  5.5128E-06

24054.31c  1.3724E-06

25055.31c  4.1191E-05

26054.31c  1.1157E-05

26056.31c  1.7344E-04

26057.31c  3.9711E-06

26058.31c  5.2948E-07

29063.31c  4.1054E-05

29065.31c  1.8299E-05

c         Water with 1335.5 PPM

m3       1001.31c  6.6737E-02

8016.31c  3.3369E-02

5010.31c  1.4821E-05

5011.31c  5.9657E-05

mt3     lwtr01.31t

totnu

prdmp     j     150

print

end of input

## D28. LEU-ST-02: LEU-SOL-THERM-002, case 2

Case 27.3-inch, Bare 1-D sphere, no impurities

c

c cell cards

1 1 9.8748e-2 -1 imp:n=1 $fuel

2 2 6.0317e-2 1 -2 imp:n=1 $Al sphere

3 0 2 imp:n=0 $outside system

c surface cards

1 so 34.4995

2 so 34.6583

mode n

kcode 5000 1.0 200 1200

ksrc 0.0 0.0 0.0

c material cards

m1      92234.31c  2.5304E-07

92235.31c  6.1604E-05

92238.31c  1.1828E-03

9019.31c  2.4893E-03

1001.31c  6.1683e-2

8016.31c 3.3331e-2

m2      13027.31c  5.9699E-02

14028.31c   5.09128E-04

14029.31c   2.57793E-05

14030.31c   1.71126E-05

29063.31c   3.55285E-05

29065.31c   1.58355E-05

25055.31c  1.4853E-05

mt1   lwtr01.31t

totnu

prdmp 320 2 0 2

print

# APENDIX E. Additional Criticality Validation

## E.1 PU-SOL-THERM-009

Case 1A, 48" Sphere 10.02 g Pu/l, 2.52 wt% Pu-240, No Imp.

1 0 2 imp:n=0                 $ Outside Everything

2 1 1.005446-01 -1 -3 imp:n=1 $ Pu(NO3)4 Solution

3 2 6.03350-02 1 -2 imp:n=1   $ Aluminum Sphere

4 0 -1 3 imp:n=1              $ Void Above Solution

1 so 60.964                   $ Sphere Inner Radius

2 so 61.734                   $ Sphere Outer Radius

3 pz 15.9558                  $ Liquid Level in Sphere

mode n

kcode 1000 1.0 10 810

ksrc     0.0 0.0 0.0 $ Point Source at origin

m1      94239.31c  2.4582E-05

94240.31c  6.3369E-07

94238.31c  1.0139E-09

94241.31c  1.8774E-08

94242.31c  3.4900E-09

8016.31c  3.4558E-02

7014.31c  7.6339E-04

1001.31c  6.5198E-02

m2      13027.31c  5.9881E-02

14028.31c   3.48353E-04

14029.31c   1.76386E-05

14030.31c   1.17087E-05

29063.31c   3.55285E-05

29065.31c   1.58355E-05

25055.31c  1.4853E-05

mt1  lwtr01.31t $ S(Alpha,Beta)

totnu

prdmp

print

## E.2 HEU-MET-FAST-73

5th Zeus Experiment 8 HEU Plates Benchmark Model (Rev) ENDF/B-VI

c Comet Hardware

1 2 0.059114 13 -16 18 -19    $ Platen & Adapter

2 2 0.059114 9 -10 -22 25     $ Alignment Tube

3 1 0.085376 2 -3 6 -7 22 -23 $ Diaphragm

c Side Reflectors

4 3 0.082784 1 -3 5 -6 26 -27 $ Front, 1st Layer

5 3 0.082784 1 -2 6 -8 26 -27 $ Left, 1st Layer

6 3 0.082784 2 -4 7 -8 26 -27 $ Back, 1st Layer

7 3 0.082784 3 -4 5 -7 26 -27 $ Right, 1st Layer

c Corner Reflectors

8 3 0.082953 2 -3 6 -7 17 -22 26 $ Below Diaphragm

9 3 0.082953 2 -3 6 -7 17 23 -28 $ Above Diaphragm

10 3 0.083394 2 -3 6 -7 28 -29   $ Top Reflector

c Column of Platters

11 3 0.083315 11 -16 19 -20      $ Bottom Reflector

12 4 0.048622 12 -15 20 -21      $ Disks w/ 1.255" Hole

13 4 0.048622 14 -15 21 -22      $ Disk w/ 3.0025" Hole

14 5 0.047810 15 -16 20 -22      $ Otr Rings, below Dia

15 4 0.048620 -15 23 -24         $ Solid Disks

16 5 0.047810 15 -16 23 -24      $ Otr Rings, above Dia

c Internal Voids

17 0 10 -17 -18 26        $ A-Tube - Refl Gap

18 0 10 -13 18 -19        $ A-Tube - Platen Gap

19 0 -9 -22 25            $ Inside Alignment Tube

20 0 10 -11 19 -22        $ A-Tube - Platter Gap

21 0 16 -17 18 -20        $ Platter-Rfl Gap (Lwr)

22 0 -16 24 -28           $ Platter - Upr Rfl Gap

23 0 2 -3 6 -7 -27 29     $ Above Top Reflector

24 0 11 -12 20 -21        $ Inside HEU Disks

25 0 11 -14 21 -22        $ Inside HEU Disk

26 0 16 -17 20 -22        $ Ring - Rfl Gap (Lwr)

27 0 16 -17 23 -28        $ Ring - Rfl Gap (Upr)

c External Voids

28 0 -1                  $ Left of Side Rfls

29 0 4                   $ Right of Side Rfls

30 0 1 -4 -5             $ Front of Side Rfls

31 0 1 -4 8              $ Behind Side Rfls

32 0 1 -4 5 -8 27        $ Above Reflectors

33 0 1 -4 5 -8 -26 #2 #19  $ Below Reflectors

1 px -44.14520           $ Left Rfl Edge

2 px -27.94000           $ Left Int Rfl Edge

3 px 27.94000            $ Right Int Rfl Edge

4 px 44.14520            $ Right Rfl Edge

5 py -44.14520           $ Front Rfl Edge

6 py -27.94000           $ Front Int Rfl Edge

7 py 27.94000            $ Back Int Rfl Edge

8 py 44.14520            $ Back Rfl Edge

9 cz 2.5400              $ 1.0-in Radius

10 cz 3.1496             $ 1.24-in. Radius

11 cz 3.1750             $ 1.25-in. Radius

12 cz 3.18770            $ 1.255-in. Radius

13 cz 4.7625             $ 1.875-in. Radius

14 cz 7.62635            $ 3.0025-in. Radius

15 cz 19.0500            $ Disk Outer Radius

16 cz 26.6700            $ Platter OR

17 cz 26.7970            $ Corner Rfl IR

c column, bottom to top

18 pz 35.73272 $ Bottom of Platen Spt

19 pz 42.08272 $ Top of Platen

20 pz 56.50992 $ Column Reflector

21 pz 57.40908 $ Lower HEU Disks & Rings

22 pz 57.70880 $ Disk with Wide Hole

23 pz 57.97296 $ Diaphragm

24 pz 59.17184 $ Upper HEU Disks & Rings

c support structure

25 pz -5.79120 $ Bottom of Alignment Tube

26 pz 0.0      $ Bottom of Reflectors

c side reflectors

27 pz 103.25100 $ Top of Side Reflectors

c corner and top reflectors

28 pz 59.24296 $ Top of Corner Reflectors

29 pz 73.67016 $ Top Reflector

mode    n

kcode   10000 1.0 50 650

c rand    hist=14285714

imp:n   1.0 26r 0.0 5r

ksrc    0.0 -15.0 56.62168  0.0 15.0 56.62168

-15.0   0.0 56.62168 15.0  0.0 56.62168

0.0 -15.0 56.92140  0.0 15.0 56.92140

-15.0   0.0 56.92140 15.0  0.0 56.92140

0.0 -15.0 57.22112  0.0 15.0 57.22112

-15.0   0.0 57.22112 15.0  0.0 57.22112

0.0 -15.0 57.55894  0.0 15.0 57.55894

-15.0   0.0 57.55894 15.0  0.0 57.55894

0.0 -15.0 58.12282  0.0 15.0 58.12282

-15.0   0.0 58.12282 15.0  0.0 58.12282

0.0 -15.0 58.42254  0.0 15.0 58.42254

-15.0   0.0 58.42254 15.0  0.0 58.42254

0.0 -15.0 58.72226  0.0 15.0 58.72226

-15.0   0.0 58.72226 15.0  0.0 58.72226

0.0 -15.0 59.02198  0.0 15.0 59.02198

-15.0   0.0 59.02198 15.0  0.0 59.02198

c SS 304

m1     6000.31c 2.0637e-4

7014.31c 1.6966e-4 7015.31c 6.3007e-7

14028.31c 9.3687e-4 14029.31c 4.7438e-5

14030.31c 3.1490e-5

15031.31c 4.2278e-5

16032.31c   5.53746E-06

16033.31c   4.43323E-08

16034.31c   2.50244E-07

16036.31c   1.16664E-09

24050.31c 7.1440e-4 24052.31c 1.3777e-2

24053.31c 1.5620e-3 24054.31c 3.8885e-4

25055.31c 1.4557e-3

26054.31c 3.5137e-3 26056.31c 5.4623e-2

26057.31c 1.2506e-3 26058.31c 1.6675e-4

28058.31c 4.4066e-3 28060.31c 1.6847e-3

28061.31c 7.2937e-5 28062.31c 2.3172e-4

28064.31c 5.8737e-5

29063.31c 1.0690e-5 29065.31c 4.7648e-6

42092.31c   2.02551E-06

42094.31c   1.26253E-06

42095.31c   2.17292E-06

42096.31c   2.27665E-06

42097.31c   1.30348E-06

42098.31c   3.29350E-06

42100.31c   1.31440E-06

c Aluminum 6061 (2.70 g/cc)

m2    12024.31c   5.21721E-04

12025.31c   6.60490E-05

12026.31c   7.27200E-05

13027.31c 5.7816e-2

14028.31c 3.1630e-4 14029.31c 1.6016e-5

14030.31c 1.0631e-5

22046.31c   2.07455E-06

22047.31c   1.87086E-06

22048.31c   1.85376E-05

22049.31c   1.36040E-06

22050.31c   1.30256E-06

24050.31c 3.3536e-6 24052.31c 6.4673e-5

24053.31c 7.3325e-6 24054.31c 1.8254e-6

25055.31c 2.1915e-5

26054.31c 5.9360e-6 26056.31c 9.2280e-5

26057.31c 2.1128e-6 26058.31c 2.8171e-7

29063.31c 4.8053e-5 29065.31c 2.1418e-5

c Copper (8.7447 g/cc)

m3    29063.31c 5.7322e-2 29065.31c 2.5549e-2

c Average Pure Inner Fuel Disks (93.28 wt.% enriched)

m4    92234.31c 5.0377e-4 92235.31c 4.5384e-2

92236.31c 1.1337e-4 92238.31c 2.6211e-3

c Average Pure Outer Fuel Rings (93.17 wt.% enriched)

m5    92234.31c 4.8707e-4 92235.31c 4.4574e-2

92236.31c 2.0675e-4 92238.31c 2.5424e-3

totnu

prdmp j 675

print

end of input

## E.3 HEU-SOL-THERM-004_case1

ol1ne 13.5 inch refl sphere based on critical volume and

c steel and refl thicknesses. enr=.9365 d sol=.997d refl=.994

c change d sigma to 1002.50 and ss to 26000.50 outer wall= 0.1 in.

c cell cards

1 1 .098526880 -1

2 3 8.7021e-02 -2 1

3 2 9.9715e-02 -3 2

4 3 8.7021e-02 -4 3

5 0 4

c surface cards

1 so 17.088

2 so 17.189

3 so 44.367

4 so 44.621

c importance card

imp:n 1.0 1.0 1.0 1.0 0.0

c material cards

m1      92234.31c  1.9029E-05

92235.31c  1.7397E-03

92238.31c  9.7761E-05

8016.31c  3.3461E-02

1001.31c  1.7849E-04

1002.31c  5.9318E-02

9019.31c  3.7129E-03

mt1    hwtr01.31t

c

c d20

m2       1001.31c  3.9886E-04

1002.31c  6.6078E-02

8016.31c  3.3238E-02

mt2    hwtr01.31t

c

c ss321

c

m3    26054.31c   3.46930E-03

26056.31c   5.44606E-02

26057.31c   1.25773E-03

26058.31c   1.67381E-04

24050.31c   7.17403E-04

24052.31c   1.38344E-02

24053.31c   1.56871E-03

24054.31c   3.90485E-04

28058.31c   5.25575E-03

28060.31c   2.02449E-03

28061.31c   8.80114E-05

28062.31c   2.80556E-04

28064.31c   7.14900E-05

25055.31c  1.7363E-03

14028.31c   1.56625E-03

14029.31c   7.93059E-05

14030.31c   5.26442E-05

sdef cel=1 rad=d2 erg=d1

sp1 -3

si2 0.0 17.088

sp2 -21 2

kcode 10000 1.0 50 550

prdmp j 100

print

## E.4 SPEC-MET-FAST-08

Np-237 sphere with HEU shells SPEC-MET-FAST-008 Simplified Bmark ENDF/B-VI

1 1 0.051054 -1             $ Np Sphere

2 2 0.059714 1 -2           $ W Clad

3 3 0.085344 2 -3           $ Ni Clad

4 4 0.052098 3 -4 -18       $ Lower Al Spacer

5 4 0.056781 6 -7 19        $ Upper Al Spacer

6 5 0.046309 4 -5 -18       $ Lower HEU Shells

7 5 0.046309 7 -8 19        $ Upper HEU Shells

8 4 0.061798 9 -11 18 -19   $ Al Shim

9 4 0.061798 5 9 -10 14 -16 $ Pedestal Ring

10 4 0.061798 -9 14 -15     $ Pedestal Center

11 4 0.061798 12 -13 17 -20 $ Homog Al Ring

c Void regions

12 0 3 -6 19

13 0 3 -9 18 -19

14 0 5 -9 15 -18

15 0 5 -12 17 -18

16 0 11 -12 18 -19

17 0 8 -12 19 -20

18 0 5 -13 16 -17

19 0 10 -13 14 -16

20 0 8 -13 20 -21

21 0 13:-14:21

1 so 4.14909        $ Radius of Np Sphere

2 so 4.42722        $ OR of W Cladding

3 so 4.81838        $ OR of Ni Cladding

4 so 5.017          $ OR of Lwr Al Liner

5 so 10.000         $ OR of Lwr HEU Shells

6 sz 0.3175 4.83108 $ IR of Upr Al Liner

7 sz 0.3175 5.013   $ OR of Upr Al Liner

8 sz 0.3175 9.668   $ OR of Upr HEU Shells

9 cz 5.080          $ IR of Al Shim

10 cz 7.620         $ IR of Al Pedestal

11 cz 10.000        $ OR of Al Shim

12 cz 10.4775       $ IR of Al Ring

13 cz 16.51         $ OR of Al Ring

14 pz -15.0622      $ Bottom of Pedestal

15 pz -10.2997      $ Top of Pedestal Ctr

16 pz -7.7597       $ Top of Pedestal Lip

17 pz -2.2225       $ Bottom of Al Ring

18 pz 0.0           $ Bottom of Al Shim

19 pz 0.3175        $ Top of Al Shim

20 pz 1.5875        $ Top of Al Ring

21 pz 10.10         $ Top Boundary

mode n

totnu

kcode 10000 1. 50 650

imp:n 1.0 19r 0.0

sdef cel=1 erg=d1

sp1 -3

c Np Sphere

m1     92233.31c 1.8577e-6 92234.31c 2.9633e-7

92235.31c 1.4074e-5 92236.31c 7.8349e-8

92238.31c 1.5626e-6

93237.31c 5.0926e-2

94238.31c 8.2304e-7 94239.31c 1.6271e-5

94240.31c 1.1619e-6 94241.31c 3.1166e-8

94242.31c 1.6032e-7

95241.31c 3.3375e-7 95243.31c 9.1575e-5

c Tungsten

m2     74182.31c 1.4057e-2 74183.31c 7.5931e-3

74184.31c 1.6254e-2 74186.31c 1.5079e-2

26054.31c 2.0349e-4 26056.31c 3.1635e-3

26057.31c 7.2430e-5 26058.31c 9.6573e-6

28058.31c 2.2406e-3 28060.31c 8.5659e-4

28061.31c 3.7086e-5 28062.31c 1.1782e-4

28064.31c 2.9865e-5

c Nickel

m3     28058.31c 5.8264e-2 28060.31c 2.2275e-2

28061.31c 9.6437e-4 28062.31c 3.0638e-3

28064.31c 7.7662e-4

c Aluminum

m4    12024.31c   5.62409E-04

12025.31c   7.12000E-05

12026.31c   7.83912E-05

13027.31c 5.5475e-2

14028.31c 3.0308e-4 14029.31c 1.5346e-5

14030.31c 1.0187e-5

22046.31c   1.98842E-06

22047.31c   1.79319E-06

22048.31c   1.77680E-05

22049.31c   1.30392E-06

22050.31c   1.24848E-06

24050.31c 2.5065e-6 24052.31c 4.8337e-5

24053.31c 5.4804e-6 24054.31c 1.3644e-6

25055.31c 2.1000e-5

26054.31c 5.6878e-6 26056.31c 8.8421e-5

26057.31c 2.0244e-6 26058.31c 2.6993e-7

29063.31c 4.6046e-5 29065.31c 2.0523e-5

c HEU

m5    92234.31c 4.7468e-4 92235.31c 4.3169e-2

92236.31c 2.1687e-4 92238.31c 2.4478e-3

prdmp j 750

print

end of input

# APENDIX F. Radiation-Shielding validation Suite

## F1. EURAC-Fe

euracos ferro

c

c  This is the input for the mcnp-3 simulation of the euracos2 iron

c  benchmark experiment.

c  Attention of Mr Sartori from Mr Rief (JRC-Ispra)   18.06.1987

c  Sent by H. de Sadeleer   JRC-Ispra   liaison officer

c

c  Several changes    Jan 2003, Steven van der Marck, NRG

c

1       0 +1

2       0 #(+2 -35 +36 -43 +44 -51)  -1

3       1 0.06294 ((+2 -3 +36 -43 +44 -51) #(+2 -3 +39 -40 +47 -48)):

((+3 -13 +36 -43 +44 -51) #(+3 -13 +38 -41 +46 -49))

4       2 0.0802 (+2 -3 +39 -40 +47 -48)

5       0 (+3 -4 +38 -41 +46 -49)

6       0 (+4 -11 +38 -41 +46 -49) #(+4 -11 -52)

7       5 0.0602 (+4 -5 -52)

8       0 (+5 -6 -52)

9       5 0.0602 (+6 -7 -52)

10      3 0.05676922 (+7 -8 -52)

11      5 0.0602 (+8 -9 -52)

12      0 (+9 -10 -52)

13      5 0.0602 (+10 -11 -52)

14      0 (+11 -12 -52)

15      0 (+11 -12 +38 -41 +46 -49) +52

16      4 0.0302177 (+12 -13 -52)

17      4 0.0302177 (+12 -13 +38 -41 +46 -49) +52

18      6 8.48765e-02  (-52 +13 -14) +53

19      6 8.48765e-02  (-52 +14 -15) +53

20      6 8.48765e-02  (-52 +15 -16) +53

21      6 8.48765e-02  (-52 +16 -17) +53

22      6 8.48765e-02  (-52 +17 -28) +53

23      6 8.48765e-02  (-52 +28 -29) +53

24      6 8.48765e-02  (-52 +29 -30) +53

25      6 8.48765e-02  (-52 +30 -31) +53

26      6 8.48765e-02  (-52 +31 -32) +53

27      6 8.48765e-02  (-52 +32 -33) +53

28      6 8.48765e-02  (-52 +33 -34) +53

29      6 8.48765e-02  (-53 +13 -14)

30      6 8.48765e-02  (-53 +14 -15)

31      6 8.48765e-02  (-53 +15 -16)

32      6 8.48765e-02  (-53 +16 -17)

33      6 8.48765e-02  (-53 +17 -28)

34      6 8.48765e-02  (-53 +28 -29) #47

35      6 8.48765e-02  (-53 +29 -30) #48

36      6 8.48765e-02  (-53 +30 -31) #49

37      6 8.48765e-02  (-53 +31 -32) #50

38      6 8.48765e-02  (-53 +32 -33) #51

39      6 8.48765e-02  (-53 +33 -34) #52

40      6 8.48765e-02 (13 -28 +38 -41 +46 -49) +52

41      6 8.48765e-02 (+28 -34 +37 -42 +45 -50) +52

42      6 8.48765e-02 (+34 -35 +37 -42 +45 -50) +52

43      6 8.48765e-02 (+34 -35 +53 -52 )

44      6 8.48765e-02 (+34 -35  -53 )

45      1 0.06294 ((+13 -28 +36 -43 +44 -51) #(13 -28 +38 -41 +46 -49))

46      1 0.06294 ((+28 -35 +36 -43 +44 -51) #(28 -35 +37 -42 +45 -50))

47      7 0.0254 (70 -71 72 -73 74 -75)

48      7 0.0254 (70 -71 72 -73 76 -77)

49      7 0.0254 (70 -71 72 -73 78 -79)

50      7 0.0254 (70 -71 72 -73 80 -81)

51      7 0.0254 (70 -71 72 -73 82 -83)

52      7 0.0254 (70 -71 72 -73 84 -85)

1       sx  100.0 400.0

2       px      -61.5

3       px      -41.0

4       px      -11.0

5       px      -10.2

6       px       -7.0

7       px       -6.8

8       px       -5.0

9       px       -4.8

10      px       -1.6

11      px       -0.8

12      px       -0.3

13      px        0.0

14      px       10.0

15      px       20.0

16      px       30.0

17      px       40.0

28      px       50.0

29      px       58.0

30      px       66.0

31      px       74.0

32      px       82.0

33      px       90.0

34      px       98.0

35      px      150.0

36      py     -120.0

37      py      -77.5

38      py      -72.5

39      py      -60.0

40      py       60.0

41      py       72.5

42      py       77.5

43      py      120.0

44      pz     -120.0

45      pz      -77.5

46      pz      -72.5

47      pz      -60.0

48      pz       60.0

49      pz       72.5

50      pz       77.5

51      pz      120.0

52      cx      40.0

53      cx      20.0

70      py      -10

71      py       10

72      pz      -10

73      pz       10

74      px       53.5

75      px       54.5

76      px       61.5

77      px       62.5

78      px       69.5

79      px       70.5

80      px       77.5

81      px       78.5

82      px       85.5

83      px       86.5

84      px       93.5

85      px       94.5

c

c  For sdef purposes (16-1-2003, SvdM)

c

101     px       -6

c  concrete

m1

1001.31c  0.0127730     $   H 1

8016.31c  0.0398531     $   O 16

5010.31c  0.000345001   $   B 10

5011.31c  0.00150100    $   B 11

20040.31c  0.00262223    $  Ca 40

20042.31c  0.0000175014  $  Ca 42

20043.31c  0.00000365176 $  Ca 43

20044.31c  0.0000565346  $  Ca 44

20046.31c  0.0000001082  $  Ca 46

20048.31c  0.00000505836 $  Ca 48

14028.31c  0.000582895   $  Si 28

14029.31c  0.0000295966  $  Si 29

14030.31c  0.0000195099  $  Si 30

13027.31c  0.000213000   $  Al

26054.31c  0.000287458   $  Fe 54

26056.31c  0.00451247    $  Fe 56

26057.31c  0.000104213   $  Fe 57

26058.31c  0.0000138688  $  Fe 58

c

c  graphite

m2

6000.31c  1            $   C

c  al-u alloy

m3

13027.31c  0.055435     $  Al

92235.31c  0.0012008    $   U 5

92238.31c  0.000133420  $   U 8

c  boral

m4

13027.31c  0.0219044    $  Al

6000.31c  0.00166186   $   C

5011.31c  0.0054043    $   B 11

5010.31c  0.00124707   $   B 10

c  al

m5

13027.31c  1            $  Al

c  fe

m6

26054.31c  0.0580      $  Fe 54

26056.31c  0.9172      $  Fe 56

26057.31c  0.0220      $  Fe 57

26058.31c  0.0028      $  Fe 58

c

c  sulphur detectors

m7         16032.31c  0.9502      $   S 32

16033.31c  0.0075      $   S 33

16034.31c  0.0421      $   S 34

16036.31c  0.0002      $   S 36

m8         16032.30y  1           $   S 32

c

c   in ---> imp:n  to set importances in MCNP-4C  (15-1-2003, SvdM)

c

imp:n    0     0     1.e-04    0.05    0.05    0.075             $  1- 6

0.1   0.2  0.2   1     1     1     1   1  0.1  1  0.1   $  7-17

1  4  19 84 370 1.2e+03 3.9e+03 1.3e+04 4.2e+04         $ 18-26

8.2e+04 1.4e+05                                         $ 27-28

1  7 53 390 2846 2.1e+04 1.0e+05 5.1e+05 2.5e+06        $ 29-37

1.2e+07 6.0e+7                                          $ 38-39

1 100 10 13400 1.0e+07 0.1 0.1                          $ 40-46

2.1e+04 1.0e+05 5.1e+05 2.5e+06 1.2e+07 6.0e+07         $ 47-52

c

c  I do not know what this MCNP-3 command would translate into

c  for MCNP-4C3. (15-1-2003, SvdM)

c

c src     40. -6.0 .029  0. 6. 7.  8.  9. 10. 11. -1. 1. 0. 0. 100.

c

c  sdef card inserted 16-1-2003 by SvdM

c

sdef  sur=101  rad=d6  erg=d1  pos=-6 0 0

c

c  The probability distribution for the radius sampling was

c  generated by 'awk', using:

c        BEGIN{ alpha = 0.029; Rmax=40.0; N=40;

c           for (i=1;i<=N;i++) {

c              r0 = (i-1)/N*Rmax; r1 = (i  )/N*Rmax;

c              p0 = ( alpha*r0*sin(alpha*r0) + cos(alpha*r0) )/(alpha**2);

c              p1 = ( alpha*r1*sin(alpha*r1) + cos(alpha*r1) )/(alpha**2);

c              printf " %10.3f %10.5g\n", r1, p1-p0;

c           }}{}END{}

c  This is because (alpha*r*sin(alpha*r) + cos(alpha*r) is the

c  primitive function of the probability function r*cos(alpha*r)

c  for the radius. (See EUR-6, pp. 26, 31, 32)

c

c  (outer) radius   probability

c

#          si6          sp6

0           0

1           0.49989

2           1.4984

3           2.4932

4           3.4816

5           4.4613

6           5.4296

7           6.3842

8           7.3225

9           8.2422

10           9.1408

11           10.016

12           10.865

13           11.686

14           12.477

15           13.235

16           13.959

17           14.645

18           15.293

19           15.899

20           16.462

21           16.981

22           17.453

23           17.876

24           18.249

25           18.57

26           18.837

27           19.05

28           19.206

29           19.305

30           19.345

31           19.325

32           19.243

33           19.1

34           18.893

35           18.623

36           18.289

37           17.889

38           17.424

39           16.892

40           16.295

c

si1     0.003355 0.004307 0.005531 0.007102 0.009119 0.01171 0.01503

0.019310 0.021870 0.023570 0.024790 0.02605  0.03183 0.04087

0.052480 0.067380 0.086520 0.1111   0.1228   0.1357  0.15

0.1657   0.1832   0.2024   0.2237   0.2472   0.2732  0.3020

0.3337   0.3688   0.4076   0.4505   0.4979   0.5502  0.6081

0.6721   0.7427   0.8209   0.9072   1.003    1.108   1.225

1.353    1.496    1.653    1.827    2.019    2.231   2.346

2.466    2.725    3.011    3.329    3.679    4.066   4.493

4.724    4.966    5.488    6.065    6.376    6.703   7.047

7.408    8.187    9.048   10.000   11.050   12.210   13.500

14.92

c

sp1    0.0 0.00003876 0.00005633 0.00008193 0.0001190 0.0001730

0.00025110 0.00036470 0.00023980 0.0001670 0.0001223

0.00013130 0.00063460 0.00111000 0.0016020 0.0023140

0.00332900 0.00477500 0.00244600 0.0028130 0.0032420

0.00373800 0.00428800 0.00492300 0.0056470

0.00647200 0.00738500 0.00843800 0.0096170 0.0109200

0.01239000 0.01400000 0.01580000 0.0177600 0.0198900

0.02219000 0.02464000 0.02723000 0.0299200 0.0326900

0.03544000 0.03812000 0.04070000 0.0431700 0.0449300

0.04660000 0.04753000 0.04772000 0.0237100 0.0235000

0.04584000 0.04361000 0.04046000 0.0366900 0.0322800

0.02757000 0.01191000 0.01072000 0.0179300 0.0135500

0.00532100 0.00445800 0.00366600 0.0029930 0.0042730

0.00256200 0.00142700 0.00072810 0.0003398 0.0001427

0.00005343

c

c erg:n      0. 20. j         $ is default in MCNP-4C ??? (15-1-2003, SvdM)

c

mode       n

cut:n      j  2.01            $ 2 MeV cut-off changed to 0.01 MeV, to allow

$ flux tallies down to 0.01 (16-1-2003, SvdM)

c

nps        1e7                $   250000

c

f4:n       47 48 49 50 51 52

fm4        (0.018836  8  103)        $  0.0188 *10^{24} atoms / gram sulphur

$      m8 is sulphur (activation data)

$  mt=103 is (n,p) activiation

print

prdmp      2j 1 2             $  get an mctal file; 2 dumps on runtpe (SvdM)

c

c  Normalise to  6.12 x 10^{11}  source neutrons per second;

c

c  tm0  6.12e11/Pi

tm0  1.948e11

t0   1e30

c

## F2. KANT

c  This is the input for the mcnp-4 simulation of the fzk kant be

c  benchmark experiment. Provided by U. Fischer, fzk

c

1     1 -8.91     (-4   9  -18) : (-9 -24)

2     2 -2.65      -4  18  -10   -1

3     1 -8.91     (-1   4    9) : (-1   7  -9   8  24)

4     0           (-1 -8 -7 24) : (1  -8 -27 -9) : (8  -7  -3  -9)

: (-1 -8  7 24)

5     0           (-7  29  3  -15) : (-30  -29  -34)

6     0            (1  27 -15  -2 -14) : (-1 10) : (1 -14 -22 -19 15)

:  (-14  22  15  -16) : (-2 14 -8 -9)

:  (-5  27 -9  2  -3) : (-8  2  -3 -9)

7     0            -5  27 -9  3 -34

8     0            (-38 -35 -34) : (-8  3  38  -9)

9     1 -8.91      (7   -6   8  1  -9  -3) : (6  8  1  -9  28 -27)

:  (26  -3  -9  -28  -27)

10    1 -8.91      (7   -6   3  -9  29)

:  (26  -34  -9   3  -27) : (30  -6  -29  -34)

11    0            (-26   6  -9  -28  -3)

12    0            (-26   6  -9   3  -34)

13    3 -7.9       (2  -3  8  5  -15  -14) : (14  -3  -11  -15  8)

:  (12 -11  -3  15  -17) : (11 -23  8 -3 -9)

14    4 -8.3        13 -12 16 -17

15    3 -7.9       (13 -12 15 -16) : (22 -21 -19 17) : (-14 22 16 -17)

:  (14 -13 15 22 -17) :(14 -22)  : (19 -20 -21)

:  (17 -2 21 -13 -20)

16    3 -7.9       (8 -23 -9 3 37) : (38 -37 8 -36) : (35 -36 -38 -34)

17    3 -7.9       5 -31 -9  3  -34

18    6 -8.90      -41  20  -44

c     --- Correction of tiny geometry error (A. Serikov, FZK, 03/08/2006)

19    8 -1.293e-3  ((11 -3 23 -9) : (11 -3 9) : (13 17 -3 -10)

:  (21 -13 44 -3) : (2 -13 -20  25  -3  17)

:  (-25  21 -20 -3  17) : (-41  44  -21)

:  (41  -3  -44  20) : (41  44  -21)

:  (13  17  -3  -20  10) : (13  44  -3)) #15

c     --- Correction of tiny geometry error (A. Serikov, FZK, 03/08/2006)

20    8 -1.293e-3  (23  31  -9  3  -33) : (9  3  -33)

:  (23  31  -9  -36  37  33) : (36  31 -39 -9 33 -34)

21    5 0.117      (36  39  -9  33  -34) : (9  33  -34)

22    0            34

c     22    8 -1.293e-3   34  -32

c     23    8 -1.293e-3   32  -40

c     24    0             40

1     so         2.7

2     so         4.5

3     so         4.9

4     cx         2.0

5     1 cx         2.8

6     1 cx         1.7

7     1 cx         1.4

8     2 cx         1.5

9     px             0

10    px           2.43

11    1 cx         4.7

12    1 cx         4.4

13    1 cx         3.9

14    1 cx         3.75

15    p   1.732  -1  0    0

16    p   1.732  -1  0  1.4

17    p   1.732  -1  0  3.2

18    px           0.55

19    px           3.8

20    px           4.0

21    s   0.693  -0.4   0.0    3.9115

22    s   0.693  -0.4   0.0    3.7583

23    2 cx         1.7

24    sx         6.7082   7.0

25    1 cx         2.836

26    1 cx         1.9

27    1 cx         2.0

28    p   1.732  -1  0   -6.8

29    p   1.732  -1  0  -10.8

30    1 cx         1.5

31    1 cx         2.95

32    so          25.

33    so           5.

34    so          22.

35    2 cx         2.3

36    2 cx         2.5

37    p   1.732   1  0  -13.8

38    p   1.732   1  0  -15.0

39    1 cx         3.0

40    so         300.

41    kx            0  0.250     +1

42    kx            0  0.06250   +1

43    p   1.732  -1  0  4.4

44    px           4.1

*tr1  0 0 0  30 120 90  60 30 90  90 90  0

*tr2  0 0 0  30  60 90 120 30 90  90 90  0

cut:n 4.0e+05 1.0e-09  0.0

c  -----------------------------------

c  FENDL-2.1 cross-section everywhere

c  in material section:

c  ----------------------------------

c     cu

m1      29063.31c    6.9170E-01

29065.31c    3.0830E-01

c     al                 mg-nat(FENDL-2.1)

m2      13027.31c   -9.7000E-01

c        12000.31c   -3.0000E-02

12024.31c  -2.36970E-02

12025.31c  -3.00000E-03

12026.31c  -3.30300E-03

c     M3: edelstahl

m3      26056.31c   -6.9930E-01

28058.31c   -9.0000E-02

24052.31c   -1.8000E-01

25055.31c   -2.0000E-02

c        6012.31c   -7.0000E-04

6000.31c   -7.0000E-04

14028.31c   -0.01

c

c     m4: 3messing ms58: 58% cu, 2% pb, 40% zn, dichte 8.3 g/cm**3

c     29000.10c -0.98    82000.60c -0.02

m4      29063.31c    6.8734E-01

29065.31c    3.0638E-01

82206.31c    1.5200E-03

82207.31c    1.3940E-03

82208.31c    3.3059E-03

c     Be EFF-3

m5       4009.31c    1.0000E+00

c     ni

m6      28058.31c    6.8270E-01

28060.31c    2.6100E-01

28061.31c    1.1300E-02

28062.31c    3.5900E-02

28064.31c    9.1000E-03

c     ni-58

m7      28058.31c    1.0000E+00

c     m8: luft ----> n-14,15 gibt nicht in FENDL deshalb: bmccs2!

c     8016.60c 0.2    7014.60c 0.8

m8       8016.31c    2.0000E-01

7014.31c    8.0000E-01

mode  n

tmp1  2.53e-8 2.53e-8 2.53e-8 2.53e-8 2.53-8 2.53-8 2.53-8 2.53-8

2.53e-8 2.53e-8 2.53e-8 2.53e-8 2.53-8 2.53-8 2.53-8 2.53-8

2.53e-8 2.53e-8 2.53e-8 2.53e-8 2.53-8 2.53-8

thtme 1.0e10

phys:n   1.4988e+01

imp:n 1 20r  0

sc1   central neutron point source in a single starting cell,

anisotropic distribution from livermore pulsed sphere setup,

table a1 in la-12212 (nov. 1991) report

for dt neutrons

sdef  pos=-0.29  0  0   cel=1 dir=d1 erg fdir d2  vec=0.866 -0.5 0

si1   a -1.0000   -0.99619  -0.98481  -0.96593  -0.93969  -0.90631

-0.86603  -0.81915  -0.76604  -0.70711  -0.64279  -0.57358

-0.50000  -0.42262  -0.34202  -0.25882  -0.17365  -0.08716

0.00000   0.08716   0.17365   0.25882   0.34202   0.42262

0.50000   0.57358   0.64279   0.70711   0.76604   0.81915

0.86603   0.90631   0.93969   0.96593   0.98481   0.99619

1.0000

sp1      0.874     0.874     0.875     0.876     0.877     0.879

0.882     0.884     0.888     0.891     0.895     0.899

0.904     0.909     0.914     0.919     0.924     0.930

0.935     0.941     0.946     0.952     0.957     0.962

0.967     0.972     0.976     0.981     0.985     0.988

0.991     0.994     0.996     0.998     0.999     1.000

1.000

ds2   q -0.99619 180 -0.98481 175 -0.96593 170 -0.93969 165 -0.90631 160

-0.86603 155 -0.81915 150 -0.76604 145 -0.70711 140 -0.64279 135

-0.57358 130 -0.50000 125 -0.42262 120 -0.34202 115 -0.25882 110

-0.17365 105 -0.08716 100  0.00000  95  0.08716  90  0.17365  85

0.25882  80  0.34202  75  0.42262  70  0.50000  65  0.57358  60

0.64279  55  0.70711  50  0.76604  45  0.81915  40  0.86603  35

0.90631  30  0.93969  25  0.96593  20  0.98481  15  0.99619  10

1.0000    5

c     si-werte fuer n-energie bei d-energie von 150kev ( heft b, s.44 )

si5   h 14.985   14.988

sp5   d   0  1

si10  h 14.975   14.985

sp10  d   0  1

si15  h 14.958   14.975

sp15  d   0  1

si20  h 14.936   14.958

sp20  d   0  1

si25  h 14.907   14.936

sp25  d   0  1

si30  h 14.872   14.907

sp30  d   0  1

si35  h 14.831   14.872

sp35  d   0  1

si40  h 14.785   14.831

sp40  d   0  1

si45  h 14.735   14.785

sp45  d   0  1

si50  h 14.680   14.735

sp50  d   0  1

si55  h 14.620   14.680

sp55  d   0  1

si60  h 14.558   14.620

sp60  d   0  1

si65  h 14.492   14.558

sp65  d   0  1

si70  h 14.425   14.492

sp70  d   0  1

si75  h 14.355   14.425

sp75  d   0  1

si80  h 14.284   14.355

sp80  d   0  1

si85  h 14.212   14.284

sp85  d   0  1

si90  h 14.140   14.212

sp90  d   0  1

si95  h 14.068   14.140

sp95  d   0  1

si100 h 13.998   14.068

sp100 d   0  1

si105 h 13.928   13.998

sp105 d   0  1

si110 h 13.861   13.928

sp110 d   0  1

si115 h 13.796   13.861

sp115 d   0  1

si120 h 13.734   13.796

sp120 d   0  1

si125 h 13.675   13.734

sp125 d   0  1

si130 h 13.620   13.675

sp130 d   0  1

si135 h 13.569   13.620

sp135 d   0  1

si140 h 13.523   13.569

sp140 d   0  1

si145 h 13.481   13.523

sp145 d   0  1

si150 h 13.444   13.481

sp150 d   0  1

si155 h 13.413   13.444

sp155 d   0  1

si160 h 13.387   13.413

sp160 d   0  1

si165 h 13.366   13.387

sp165 d   0  1

si170 h 13.352   13.366

sp170 d   0  1

si175 h 13.343   13.352

sp175 d   0  1

si180 h 13.340   13.343

sp180 d   0  1

fc11  current through surfaces  34

f11:n  34

c     grobeinteilung fuer leakage-integrale 15Mev bis 1.e-09Mev

c      f. 5/4/95

E11               1.000E-07  4.140E-07  5.316E-07  6.826E-07  8.764E-07

1.125E-06  1.445E-06  1.855E-06  2.382E-06  3.059E-06  3.928E-06

5.044E-06  6.476E-06  8.315E-06  1.068E-05  1.371E-05  1.760E-05

2.260E-05  2.902E-05  3.727E-05  4.785E-05  6.144E-05  7.889E-05

1.013E-04  1.301E-04  1.670E-04  2.145E-04  2.754E-04  3.536E-04

4.540E-04  5.829E-04  7.485E-04  9.611E-04  1.234E-03  1.585E-03

2.035E-03  2.249E-03  2.485E-03  2.613E-03  2.747E-03  3.035E-03

3.355E-03  3.707E-03  4.307E-03  5.531E-03  7.102E-03  9.119E-03

1.060E-02  1.171E-02  1.503E-02  1.931E-02  2.188E-02  2.358E-02

2.418E-02  2.479E-02  2.606E-02  2.700E-02  2.850E-02  3.183E-02

3.431E-02  4.087E-02  4.631E-02  5.248E-02  5.656E-02  6.738E-02

7.200E-02  7.950E-02  8.250E-02  8.652E-02  9.804E-02  1.111E-01

1.168E-01  1.228E-01  1.291E-01  1.357E-01  1.426E-01  1.500E-01

1.576E-01  1.657E-01  1.742E-01  1.832E-01  1.926E-01  2.024E-01

2.128E-01  2.237E-01  2.352E-01  2.472E-01  2.732E-01  2.873E-01

2.945E-01  2.972E-01  2.985E-01  3.020E-01  3.337E-01  3.688E-01

3.877E-01  4.076E-01  4.505E-01  4.979E-01  5.234E-01  5.502E-01

5.784E-01  6.081E-01  6.393E-01  6.721E-01  7.065E-01  7.427E-01

7.808E-01  8.209E-01  8.629E-01  9.072E-01  9.616E-01  1.003E+00

1.108E+00  1.165E+00  1.225E+00  1.287E+00  1.353E+00  1.423E+00

1.496E+00  1.572E+00  1.653E+00  1.738E+00  1.827E+00  1.920E+00

2.019E+00  2.123E+00  2.231E+00  2.307E+00  2.346E+00  2.365E+00

2.385E+00  2.466E+00  2.592E+00  2.725E+00  2.865E+00  3.012E+00

3.166E+00  3.329E+00  3.679E+00  4.066E+00  4.493E+00  4.724E+00

4.966E+00  5.221E+00  5.488E+00  5.770E+00  6.065E+00  6.376E+00

6.592E+00  6.703E+00  7.047E+00  7.408E+00  7.788E+00  8.187E+00

8.607E+00  9.048E+00  9.512E+00  1.000E+01  1.051E+01  1.105E+01

1.162E+01  1.221E+01  1.252E+01  1.284E+01  1.350E+01  1.384E+01

1.419E+01  1.455E+01  1.492E+01  1.568E+01  1.649E+01  1.690E+01

1.733E+01  1.964E+01

print

prdmp  j -30 1 5

c     dbcn  2j 1 100

nps   10000000

ctme  360.

## F3. NIST

### F3.1 NoCd+NoWater+2,0"

det at 3 inch model  no cadmium except bucket; no water

c     two fission chambers and stems, source and holder included

c     support structure, bucket, steel sphere and weld

c    fission chamber on +z side

1 1 -21.45  -1 2 -3

2 2 -2.700   3 -5 -1 4

3 2 -2.700   6 -3 -2 4

4 3 -2.2     7 -5 -4 8

5 2 -2.700  10 -11 -8 9

6 2 -2.700  13 -10 -12 14

7 2 -2.700     -11 -9 15

8 3 -2.2    16 -5 -15 17

9 3 -2.2    11 -5  -19 15

10 3 -2.2    22 -5 -23 1

11 3 -2.2    11 -5 -24 23

12 2 -2.700  10 -11 -25 23

13 2 -2.700  13 -10 -26 27

14 3 -2.2    16 -11 -29 28

15 3 -2.2    11  -5 -29 30

16 2 -2.700     -11 -28 25

21 2 -2.700  18 -32 -33 31

22 2 -2.700     -32 -34 33

24 2 -2.700   5 -18 -33 21

25 2 -2.700      -5 -20 21

26 2 -2.700 -35 18 501 -502   $ stem (I think)

c     following cells are void cells

50 0 (-6 -2 9):(6 -7 -4 9)

51 0 (-16 -15 20):(16 -5 -17 20)

52 0 11 -5 -8 19

53 0 (7 -13 -8 9):(13 -10 -14 9):(13 -10 -8 12)

54 0 11 -5  -30 24

55 0 (-22 -25 1) : (22 -13 -25 23)

56 0 (-16 -33 28) : (16 -5 -33 29)

57 0 13 -10 -25 26

58 0 13 -10 -27 23

c

c    cells in source

60 4 -1.85    -50 -51 52  $ cf2o2so4

61 5 -2.00    -53 -54 51  $ al powder

62 0        50 -53 -51 52  $ air-filled cell

63 2 -2.700 53 -55 -54 52

64 2 -2.700    -55 -52 56

65 0        55 -57 -54 56  $ air-filled cell

66 6 -7.92 57 -58 -54 56  $ stainless steel

67 6 -7.92    -58 -56 59  $ stainless steel

68 6 -7.92 60 -58 -61 54  $ stainless steel

69 0           -60 -61 54 $ air-filled cell

70 6 -7.92    -58 -62 61  $ ss

71 6 -7.92    -63 -64 62  $ ss

72 6 -7.92 65 -58 -66 62  $ ss

c    cells in source holder

73 6 -7.92 63 -67 -68 69   $ ss

74 6 -7.92 70 -55 -71 68   $ ss

75 6 -7.92 72 -55 -73 71   $ ss

76 6 -7.92 72 -74 -75 73   $ ss

77 6 -7.92 72 -76 -77 75   $ ss

78 6 -7.92    -76 -78 77   $ ss

79 6 -7.92    -53 -79 78   $ ss

80 6 -7.92    -80 -81 79   $ ss chain

81 0        63 -70 -64 68   $ no water

82 0           -70 -71 64   $ no water

83 0           -72 -73 71   $ no water

84 0           -72 -77 73 $ air-filled void

85 2 -2.700 -92 -90 91 80  $ item W al plate,preamps,cable

86 2 -2.700 -95 -93 94 80  $ item V support ring & attachments Al

87 9 -2.717 96 -97 -98 99  $ item U fission chamber brace Al+H

88 6 -7.92  82 -83 -73     $ ss sphere shell

c    cd and al bucket cells

89 8 -8.65  151 -152 157 -156

90 8 -8.65  150 -152 156 -155

91 8 -8.65      -152 158 -157

92 2 -2.700 152 -153 158 -155

93 2 -2.700 150 -153 155 -154

94 2 -2.700     -153 159 -158

c    end of bucket

c    bead weld on ss sphere

95 6 -7.92 83 -160 -161 162  $ ss weld

96 0 (83 -160 161 74):(83 -160 -162) $ void outside weld

c    end of weld

c    outside world to make it easier to add source and holder to big file

800 0     (58 -74 -62 59):(58 -74 -66 62):(63 -65 -66 62) $ no h2o in sphere

801 0        63 -74 -69 66          $ no h2o in sphere

802 0        (67 -74 -68 69):(55 -74 -73 -82 68) $ no h2o in sphere

803 0 (76 -74 -78 75):(53 -74 -79 78):(80 -74 -94 79)

804 0 80 -74 -91 93

805 0 80 -74 -81 90

806 0 -73 -74 83 501

c

c    cells for fission chamber on -z side

101 1 -21.45  101 -102 -3

102 2 -2.700   3 -5 101 -104

103 2 -2.700   6 -3 102 -104

104 3 -2.2     7 -5 104 -108

105 2 -2.700  10 -11 108 -109

106 2 -2.700  13 -10 112 -114

107 2 -2.700     -11 109 -115

108 3 -2.2    16 -5 115 -117

109 3 -2.2    11 -5  119 -115

110 3 -2.2    22 -5 123 -101

111 3 -2.2    11 -5 124 -123

112 2 -2.700  10 -11 125 -123

113 2 -2.700  13 -10 126 -127

114 3 -2.2    16 -11 129 -128

115 3 -2.2    11  -5 129 -130

116 2 -2.700     -11 128 -125

121 2 -2.700  18 -32 133 -131

122 2 -2.700     -32 134 -133

124 2 -2.700   5 -18 133 -121

125 2 -2.700      -5 120 -121

126 2 -2.700 -135 18 501 -502

c     following cells are void cells

150 0 (-6 102 -109):(6 -7 104 -109)

151 0 (-16 115 -120):(16 -5 117 -120)

152 0 11 -5 108 -119

153 0 (7 -13 108 -109):(13 -10 114 -109):(13 -10 108 -112)

154 0 11 -5  130 -124

155 0 (-22 125 -101) : (22 -13 125 -123)

156 0 (-16 133 -128) : (16 -5 133 -129)

157 0 13 -10 125 -126

158 0 13 -10 127 -123

c    outside world cells 1000s are +z and + and -y

1000 0 ((32:34:-21)(35:502) 501 500 74 -156 -151 160) #87 $ +z +y with stem

1001 0 (-21:32:34) -501 500 160 -151 157 $ +z -y w/o stem +160

1002 0 18 -32 -31 21 -501  $fission chamber cutout +z -y without stem

1003 0 -32 18 35 21 -31 501       $fission chamber +z +y with stem

1004 0 ((-91 93 74 500):(-93 94 95 500)) -1000  $ between cell 85 and 86

1005 0 ((-81 90 74 500):(-90 91 92 500):(81 500)) -1000  $ above cell 85

1006 0        501 500 74 -82          $+z +y inside sphere no water

1007 0        (-59:74) 500 -501 -82   $ +z -y inside sphere no water

1008 0 ((156 -154 74 -150):(154 -94 74)) 500 -1000 $ above bucket +z

c    outside world cells 1050s are -z and + and -y

1050 0 ((32:-134:121) (135:502) 501 -500 74 -156 -151 160) #87 $-z +y stem

1051 0 (121:32:-134) -501 -500 160 -151 157 $ -z -y w/o stem

1052 0 18 -32 131 -121 -501  $ fission chamber cutout -z -y without stem

1053 0 18 -32 135 -121 131 501      $ fission chamber -z +y with stem

1054 0 ((-91 93 74 -500):(-93 94 95 -500)) -1000 $ between cell 85 and 86

1055 0 ((-90 91 92 -500):(-81 90 74 -500):(81 -500)) -1000 $ above cell 85

1056 0        501 -500 74 -82         $-z +y inside sphere no water

1057 0        (-59:74) -500 -501 -82  $ -z -y inside sphere no water

1058 0 ((156 -154 74 -150):(154 -94 74)) -500 -1000 $ above bucket -z

2000 0 (153:-159) -154 -1000

2001 0 1000  $outside world

1 pz 7.634

2 pz 7.606

3 cz 0.953

4 pz 7.558

5 cz 1.193

6 cz 0.921

7 cz 1.016

8 pz 7.507

9 pz 7.126

10 cz 1.101

11 cz 1.149

12 pz 7.471

13 cz 1.063

14 pz 7.253

15 pz 7.113

16 cz 0.874

17 pz 7.075

18 cz 1.247

19 pz 7.329

20 pz 7.056

21 pz 7.005

22 cz 0.857

23 pz 7.710

24 pz 7.837

25 pz 8.091

26 pz 7.964

27 pz 7.746

28 pz 8.104

29 pz 8.142

30 pz 7.888

31 pz 8.432

32 cz 1.786

33 pz 8.529

34 pz 8.583

35 c/y 0 7.62 .21035

c    surfaces of source and source holder

50 cy  0.10

51 py  0.04

52 py -0.04

53 cy  0.127

54 py  0.506

55 cy  0.318

56 py -0.154

57 cy  0.330

58 cy  0.381

59 py -0.205

60 cy  0.152

61 py  0.563

62 py  0.608

63 cy  0.114

64 py  2.289

65 cy  0.277

66 py  0.659

67 cy  0.366

68 py  2.108

69 py  1.613

70 cy  0.254

71 py  2.616

72 cy  0.300

73 py  5.048

74 cy  1.270

75 py  5.174

76 cy  0.445

77 py  5.428

78 py  5.555

79 py  6.190

80 cy  0.159

81 py 79.000

c     end of surfaces for source and holder

c    surfaces of water filled sphere

82 so 5.080

83 so 5.126

c    end of sphere

c    surfaces for miscellaneous support stuff

90 py 74.79

91 py 73.66

92 cy 20.01

93 py 30.665

94 py 30.480

95 cy 14.446

96 cy 7.858

97 cy 8.493

98 py 11.667

99 py 11.430

c    end of misc support surfaces

c    following surfaces are for fission chamber on -z side

101 pz -7.634

102 pz -7.606

104 pz -7.558

108 pz -7.507

109 pz -7.126

112 pz -7.471

114 pz -7.253

115 pz -7.113

117 pz -7.075

119 pz -7.329

120 pz -7.056

121 pz -7.005

123 pz -7.710

124 pz -7.837

125 pz -8.091

126 pz -7.964

127 pz -7.746

128 pz -8.104

129 pz -8.142

130 pz -7.888

131 pz -8.432

133 pz -8.529

134 pz -8.583

135 c/y 0 -7.62 .21035

c    bucket surfaces

150 cy 2.54

151 cy 34.290

152 cy 34.341

153 cy 34.376

154 py 22.946

155 py 22.911

156 py 22.86

157 py -22.86

158 py -22.911

159 py -22.946

c    end of bucket

c    weld surfaces

160 so 5.276

161 1 pz 0.08

162 1 pz -0.08

c    end of weld

500 pz 0

501 py 0

502 py 21.59   $ top of stem

1000 s 0 27 0 65

1001 cz 0.635

m1      78000.31c    1.0000E+00

m2      13027.31c    1.0000E+00

m3       6000.31c    2.0000E+00

9019.31c    3.0000E+00

17035.31c   7.57700E-01

17037.31c   2.42300E-01

m4      98252.31c    2.0000E+00

8016.31c    6.0000E+00

16032.31c    1.0000E+00

m5      13027.31c    1.0000E+00

m6    26054.31c   4.06227E-02

26056.31c   6.37690E-01

26057.31c   1.47271E-02

26058.31c   1.95990E-03

24050.31c   8.25550E-03

24052.31c   1.59199E-01

24053.31c   1.80519E-02

24054.31c   4.49350E-03

28058.31c   6.46731E-02

28060.31c   2.49119E-02

28061.31c   1.08300E-03

28062.31c   3.45230E-03

28064.31c   8.79700E-04

25055.31c    2.0000E-02

c       m7 1001.50c 2 8016.50c 1            $  no water

c      mt7 lwtr.07

m8    48106.31c   1.25000E-02

48108.31c   8.90000E-03

48110.31c   1.24900E-01

48111.31c   1.28000E-01

48112.31c   2.41300E-01

48113.31c   1.22200E-01

48114.31c   2.87300E-01

48116.31c   7.49000E-02

m9      13027.31c    1.0000E+00

1001.31c    1.7000E-01

mode n

*tr1  0 0 0   0 90 90 90 45 135 90 45 45

sdef erg=d1 pos 0 0 0 cel=60 rad=d2 ext=d3 axs 0 1 0

si1 0. 0.05 0.1 0.2 0.25 0.3 0.4 0.5 0.6 0.7 0.8

1.0 1.2 1.4 1.5 1.6 1.8 2.0 2.2 2.3 2.4 2.6 2.8 3.0

3.4 3.7 4.2 4.6 5.0 5.5 6.0 6.5 7.0 7.5 8.0 8.5

9.0 9.5 10. 11. 12. 13. 14. 16. 18.

sp1 0 0.0039 0.0074 0.0219 0.0140 0.0152 0.0323 0.0337 0.0343 0.0343

0.0338 0.0664 0.0641 0.0608 0.0290 0.0279 0.0527 0.0484

0.0442 0.0206 0.0196 0.0364 0.0328 0.0296 0.0503 0.0310

0.0413 0.0253 0.0200 0.0190 0.0140 0.0102 0.00734 0.00527

0.00378 0.00270 0.00193 0.00137 0.00098 0.00118 0.00059

0.00030 0.00015 0.00011 0.00003

si2 0 .1

si3 0.04

c     low energy reactions

fc2 low energy reactions

f2:n (1 101) (2 102)

fs2 -1001

fm2 (1 101 -6)(1 102 -6)

tf2 1 1 j 1 1 3j  $ 1st cell,total,j,1st seg,1st mult,j,last energy

c     high energy reaction rates

fc12  high energy reactions

f12:n (1 101) (2 102)

fs12 -1001

fm12 (1 103 -6)(1 104 -6)

tf12 1 1 j 1 1 3j  $  1st cell,total,j,1st seg,1st mult,j,last energy,j

m101    92235.31c    1.0000E+00

m102    94239.31c    1.0000E+00

m103    92238.31c    1.0000E+00

m104    93237.31c    1.0000E+00

imp:n 1 122r 0

prdmp j -60

ctme 180

print

### F3.2 Cd+Water+2,5"

5-inch diam water sphere; cadmium-covered with lite water; all 4 foil materials

c     file run for nist calculation; 27- and 4-group bins; also flux

c     surfaces 1&101, 2&102 added in tally; imp set by hand; split 100-1

c     two fission chambers and stems, source and holder included

c     support structure, bucket, steel sphere and weld

c    fission chamber on +z side

1 1 -21.45  -1 2 -3      imp:n=800

2 2 -2.700   3 -5 -1 4   imp:n=800

3 2 -2.700   6 -3 -2 4   imp:n=800

4 3 -2.2     7 -5 -4 8   imp:n=800

5 2 -2.700  10 -11 -8 9  imp:n=800

6 2 -2.700  13 -10 -12 14   imp:n=800

7 2 -2.700     -11 -9 15  imp:n=800

8 3 -2.2    16 -5 -15 17  imp:n=800

9 3 -2.2    11 -5  -19 15   imp:n=800

10 3 -2.2    22 -5 -23 1  imp:n=800

11 3 -2.2    11 -5 -24 23  imp:n=800

12 2 -2.700  10 -11 -25 23  imp:n=800

13 2 -2.700  13 -10 -26 27  imp:n=800

14 3 -2.2    16 -11 -29 28  imp:n=800

15 3 -2.2    11  -5 -29 30  imp:n=800

16 2 -2.700     -11 -28 25  imp:n=800

22 2 -2.700      -5 -34 29  imp:n=800  $ changed for cd covered

24 2 -2.700   5 -18 -29 21  imp:n=800

25 2 -2.700      -5 -20 21  imp:n=800

26 2 -2.700     -31 -21 38  imp:n=800 $ cd cover fission chamber cells

27 2 -2.700  18 -31 -20 21  imp:n=800 $ cd cover fission chamber cells

28 8 -8.65      -31 -38 39  imp:n=800 $ cd cover fission chamber cells

29 8 -8.65   31 -32 -37 39 501  imp:n=800 $ cd cover fission chamber cells

30 8 -8.65   31 -32 -37 39 -501  imp:n=800 $below stem

31 8 -8.65      -31 -37 36  imp:n=800 $ cd cover fission chamber cells

32 2 -2.700 -35 32 501 -502   imp:n=8 $ stem +z+y

33 8 -8.865   41 -40 32 -43 501   imp:n=800 $cd liner on stem

34 8 -8.865   41 -42 43 -44 501   imp:n=8 $cd liner on stem

c     following cells are void cells

50 0 (-6 -2 9):(6 -7 -4 9)    imp:n=800

51 0 (-16 -15 20):(16 -5 -17 20)    imp:n=800

52 0 11 -5 -8 19    imp:n=800

53 0 (7 -13 -8 9):(13 -10 -14 9):(13 -10 -8 12)    imp:n=800

54 0 11 -5  -30 24    imp:n=800

55 0 (-22 -25 1) : (22 -13 -25 23)    imp:n=800

56 0 (-16 -29 28)    imp:n=800

57 0 13 -10 -25 26    imp:n=800

58 0 13 -10 -27 23    imp:n=800

c

c    cells in source

60 4 -1.85    -50 -51 52  imp:n=1  $ cf2o2so4

61 5 -2.00    -53 -54 51  imp:n=1  $ al powder

62 0        50 -53 -51 52  imp:n=1  $ air-filled cell

63 2 -2.700 53 -55 -54 52  imp:n=1

64 2 -2.700    -55 -52 56  imp:n=1

65 0        55 -57 -54 56  imp:n=1  $ air-filled cell

66 6 -7.92 57 -58 -54 56  imp:n=1  $ stainless steel

67 6 -7.92    -58 -56 59  imp:n=1  $ stainless steel

68 6 -7.92 60 -58 -61 54  imp:n=1  $ stainless steel

69 0           -60 -61 54 imp:n=1  $ air-filled cell

70 6 -7.92    -58 -62 61  imp:n=1  $ ss

71 6 -7.92    -63 -64 62  imp:n=1  $ ss

72 6 -7.92 65 -58 -66 62  imp:n=1  $ ss

c    cells in source holder

73 6 -7.92 63 -67 -68 69   imp:n=1  $ ss

74 6 -7.92 70 -55 -71 68   imp:n=1  $ ss

75 6 -7.92 72 -55 -73 71   imp:n=1  $ ss

76 6 -7.92 72 -74 -75 73   imp:n=1  $ ss

77 6 -7.92 72 -76 -77 75   imp:n=1  $ ss

78 6 -7.92    -76 -78 77   imp:n=1  $ ss

79 6 -7.92    -53 -79 78   imp:n=1  $ ss

80 6 -7.92    -80 -81 79   imp:n=1  $ ss chain

81 7 -1.000 63 -70 -64 68   imp:n=1  $ water

82 7 -1.000    -70 -71 64   imp:n=1  $ water

83 7 -1.000    -72 -73 71   imp:n=1  $ water

84 0           -72 -77 73 imp:n=1  $ air-filled void

85 2 -2.700 -92 -90 91 80  imp:n=1  $ item W al plate,preamps,cable

86 2 -2.700 -95 -93 94 80  imp:n=1  $ item V support ring & attachments Al

87 9 -2.717 96 -97 -98 99  imp:n=1  $ item U fission chamber brace Al+H

88 6 -7.92  82 -83 -73     imp:n=8  $ ss sphere shell

c    cd and al bucket cells

89 8 -8.65  151 -152 157 -156  imp:n=1

90 8 -8.65  150 -152 156 -155  imp:n=1

91 8 -8.65      -152 158 -157  imp:n=1

92 2 -2.700 152 -153 158 -155  imp:n=1

93 2 -2.700 150 -153 155 -154  imp:n=1

94 2 -2.700     -153 159 -158  imp:n=1

c    end of bucket

c    bead weld on ss sphere

95 6 -7.92 83 -160 -161 162  imp:n=1  $ ss weld

96 0 (83 -160 161 74):(83 -160 -162) imp:n=8  $ void outside weld

c    end of weld

c    outside world to make it easier to add source and holder to big file

800 7 -1.000 (58 -74 -62 59):(58 -74 -66 62):(63 -65 -66 62)

imp:n=1$h20 in sphere

801 7 -1.000 63 -74 -69 66          imp:n=1 $ h20 in sphere

802 7 -1.000 (67 -74 -68 69):(55 -74 -73 -82 68) imp:n=1 $ h20 in sphere

803 0 (76 -74 -78 75):(53 -74 -79 78):(80 -74 -94 79)  imp:n=1

804 0 80 -74 -91 93  imp:n=1

805 0 80 -74 -81 90  imp:n=1

806 0 -73 -74 83 501  imp:n=1

c

c    cells for fission chamber on -z side

101 1 -21.45  101 -102 -3     imp:n=800

102 2 -2.700   3 -5 101 -104     imp:n=800

103 2 -2.700   6 -3 102 -104     imp:n=800

104 3 -2.2     7 -5 104 -108     imp:n=800

105 2 -2.700  10 -11 108 -109     imp:n=800

106 2 -2.700  13 -10 112 -114     imp:n=800

107 2 -2.700     -11 109 -115     imp:n=800

108 3 -2.2    16 -5 115 -117     imp:n=800

109 3 -2.2    11 -5  119 -115     imp:n=800

110 3 -2.2    22 -5 123 -101     imp:n=800

111 3 -2.2    11 -5 124 -123     imp:n=800

112 2 -2.700  10 -11 125 -123     imp:n=800

113 2 -2.700  13 -10 126 -127     imp:n=800

114 3 -2.2    16 -11 129 -128     imp:n=800

115 3 -2.2    11  -5 129 -130     imp:n=800

116 2 -2.700     -11 128 -125     imp:n=800

122 2 -2.700      -5 134 -129     imp:n=800

124 2 -2.700   5 -18 129 -121     imp:n=800

125 2 -2.700      -5 120 -121     imp:n=800

126 2 -2.700     -31 121 -138     imp:n=800

127 2 -2.700  18 -31 120 -121     imp:n=800

128 8 -8.65      -31 138 -139     imp:n=800

129 8 -8.65   31 -32 137 -139 501     imp:n=800

130 8 -8.65   31 -32 137 -139 -501     imp:n=800

131 8 -8.65      -31 137 -136     imp:n=800

132 2 -2.700 -135 32 501 -502  imp:n=8 $ stem -z+y

133 8 -8.865  141 -140 32 -43 501   imp:n=800 $cd liner on stem -z+y

134 8 -8.865  141 -142 43 -44 501   imp:n=8 $cd liner on stem -z+y

c     following cells are void cells

150 0 (-6 102 -109):(6 -7 104 -109)                  imp:n=800

151 0 (-16 115 -120):(16 -5 117 -120)                 imp:n=800

152 0 11 -5 108 -119                                      imp:n=800

153 0 (7 -13 108 -109):(13 -10 114 -109):(13 -10 108 -112)   imp:n=800

154 0 11 -5  130 -124                                     imp:n=800

155 0 (-22 125 -101) : (22 -13 125 -123)                   imp:n=800

156 0 (-16 129 -128)                                   imp:n=800

157 0 13 -10 125 -126                                   imp:n=800

158 0 13 -10 127 -123                                   imp:n=800

c     splitting cells in water

200 7 -1.000 170 -171 501 -82   imp:n=4

201 7 -1.000 171 -172 501 -82   imp:n=4

202 7 -1.000 172 -173 501 -82   imp:n=8

203 7 -1.000 173      501 -82   imp:n=8

204 7 -1.000 170 -171 -501 -82   imp:n=4

205 7 -1.000 171 -172 -501 -82   imp:n=4

206 7 -1.000 172 -173 -501 -82   imp:n=8

207 7 -1.000 173      -501 -82   imp:n=8

208 7 -1.000 -174 175 501 -82   imp:n=4

209 7 -1.000 -175 176 501 -82   imp:n=4

210 7 -1.000 -176 177 501 -82   imp:n=8

211 7 -1.000 -177     501 -82   imp:n=8

212 7 -1.000 -174 175 -501 -82   imp:n=4

213 7 -1.000 -175 176 -501 -82   imp:n=4

214 7 -1.000 -176 177 -501 -82   imp:n=8

215 7 -1.000 -177     -501 -82   imp:n=8

c    end of splitting cells

c    outside world cells 1000s are +z and + and -y

1000 0 ((32:37:-39)(35:502) 501 500 74 -156 -151 160) #87 $ +z +y with stem

#33 #34            imp:n=8

1001 0 (-39:32:37) -501 500 160 -151 157

imp:n=8  $ +z -y w/o stem +160

1002 0 ((18 -31 -36 20):(5 -18 -36 29):(-5 -36 34)) -501

imp:n=800  $ cutout +z-y wo stem

1003 0 ((-31 18 20 -29):(-31 5 -36 29):(-5 -36 34)) 501

imp:n=800  $ fc +z+y with stem

1004 0 ((-91 93 74 500):(-93 94 95 500)) -1000

imp:n=1  $ between cell 85 and 86

1005 0 ((-81 90 74 500):(-90 91 92 500):(81 500)) -1000

imp:n=1  $ above cell 85

1006 7 -1.000 501 500 74 -82 -170 imp:n=2  $+z +y inside sphere water

1007 7 -1.000 (-59:74) 500 -501 -82 -170

imp:n=2  $ +z -y inside sphere water

1008 0 ((156 -154 74 -150):(154 -94 74)) 500 -1000

imp:n=1  $ above bucket +z

c    outside world cells 1050s are -z and + and -y

1050 0 ((32:-137:139) (135:502) 501 -500 74 -156 -151 160) #87 $-z +y stem

#133 #134                    imp:n=8

1051 0 (139:32:-137) -501 -500 160 -151 157

imp:n=8  $ -z -y w/o stem

1052 0 ((18 -31 136 -120):(5 -18 136 -129):(-5 136 -134)) -501 $

imp:n=800

1053 0 ((-31 18 -120 129):(-31 5 136 -129):(-5 136 -134)) 501

imp:n=800

1054 0 ((-91 93 74 -500):(-93 94 95 -500)) -1000

imp:n=1  $ between cell 85 and 86

1055 0 ((-90 91 92 -500):(-81 90 74 -500):(81 -500)) -1000

imp:n=1  $ above cell 85

1056 7 -1.000 501 -500 74 -82 174

imp:n=2  $-z +y inside sphere water

1057 7 -1.000 (-59:74) -500 -501 -82 174

imp:n=2   $ -z -y inside sphere water

1058 0 ((156 -154 74 -150):(154 -94 74)) -500 -1000

imp:n=1 $ above bucket -z

2000 0 (153:-159) -154 -1000               imp:n=1

2001 0 1000                    imp:n=0  $  outside world

1 pz 9.539

2 pz 9.511

3 cz 0.953

4 pz 9.463

5 cz 1.193

6 cz 0.921

7 cz 1.016

8 pz 9.412

9 pz 9.031

10 cz 1.101

11 cz 1.149

12 pz 9.376

13 cz 1.063

14 pz 9.158

15 pz 9.018

16 cz 0.874

17 pz 8.980

18 cz 1.247

19 pz 9.234

20 pz 8.961

21 pz 8.910

22 cz 0.857

23 pz 9.615

24 pz 9.742

25 pz 9.996

26 pz 9.869

27 pz 9.651

28 pz 10.009

29 pz 10.047

30 pz 9.793

31 cz 1.511

32 cz 1.588

34 pz 10.100

35 c/y 0 9.525 .21035

36 pz 10.470

37 pz 10.549

38 pz 8.882

39 pz 8.804

40 c/y 0 9.525 0.820

41 c/y 0 9.525 0.238

42 c/y 0 9.525 0.318

43 py 1.689

44 py 7.582

c    surfaces of source and source holder

50 cy  0.10

51 py  0.04

52 py -0.04

53 cy  0.127

54 py  0.506

55 cy  0.318

56 py -0.154

57 cy  0.330

58 cy  0.381

59 py -0.205

60 cy  0.152

61 py  0.563

62 py  0.608

63 cy  0.114

64 py  2.289

65 cy  0.277

66 py  0.659

67 cy  0.366

68 py  2.108

69 py  1.613

70 cy  0.254

71 py  2.616

72 cy  0.300

73 py  6.334

74 cy  1.270

75 py  6.460

76 cy  0.445

77 py  6.714

78 py  6.841

79 py  7.476

80 cy  0.159

81 py 80.286

c     end of surfaces for source and holder

c    surfaces of water filled sphere

82 so 6.350

83 so 6.396

c    end of sphere

c    surfaces for miscellaneous support stuff

90 py 74.79

91 py 73.66

92 cy 20.01

93 py 30.665

94 py 30.480

95 cy 14.446

96 cy 7.858

97 cy 8.493

98 py 11.667

99 py 11.430

c    end of misc support surfaces

c    following surfaces are for fission chamber on -z side

101 pz -9.539

102 pz -9.511

104 pz -9.463

108 pz -9.412

109 pz -9.031

112 pz -9.376

114 pz -9.158

115 pz -9.018

117 pz -8.980

119 pz -9.234

120 pz -8.961

121 pz -8.910

123 pz -9.615

124 pz -9.742

125 pz -9.996

126 pz -9.869

127 pz -9.651

128 pz -10.009

129 pz -10.047

130 pz -9.793

134 pz -10.100

135 c/y 0 -9.525 .21035

136 pz -10.470

137 pz -10.549

138 pz -8.882

139 pz -8.804

140 c/y 0 -9.525 0.820

141 c/y 0 -9.525 0.238

142 c/y 0 -9.525 0.318

c    bucket surfaces

150 cy 2.54

151 cy 34.290

152 cy 34.341

153 cy 34.376

154 py 22.946

155 py 22.911

156 py 22.86

157 py -22.86

158 py -22.911

159 py -22.946

c    end of bucket

c    weld surfaces

160 so 6.546

161 1 pz 0.08

162 1 pz -0.08

c    end of weld

c    surfaces for variance reduction

170 pz  1.3

171 pz  2.54

172 pz  3.81

173 pz  5.08

174 pz -1.3

175 pz -2.54

176 pz -3.81

177 pz -5.08

c    end of splitting surfaces

500 pz 0

501 py 0

502 py 21.59   $ top of stem

1000 s 0 27 0 65

1001 cz 0.635

m1      78000.31c    1.0000E+00

m2      13027.31c    1.0000E+00

m3       6000.31c    2.0000E+00

9019.31c    3.0000E+00

17035.31c   7.57700E-01

17037.31c   2.42300E-01

m4      98252.31c    2.0000E+00

8016.31c    6.0000E+00

16032.31c    1.0000E+00

m5      13027.31c    1.0000E+00

m6    26054.31c   4.06227E-02

26056.31c   6.37690E-01

26057.31c   1.47271E-02

26058.31c   1.95990E-03

24050.31c   8.25550E-03

24052.31c   1.59199E-01

24053.31c   1.80519E-02

24054.31c   4.49350E-03

28058.31c   6.46731E-02

28060.31c   2.49119E-02

28061.31c   1.08300E-03

28062.31c   3.45230E-03

28064.31c   8.79700E-04

25055.31c    2.0000E-02

m7       1001.31c    2.0000E+00

8016.31c    1.0000E+00

mt7 lwtr01.31t

m8    48106.31c   1.25000E-02

48108.31c   8.90000E-03

48110.31c   1.24900E-01

48111.31c   1.28000E-01

48112.31c   2.41300E-01

48113.31c   1.22200E-01

48114.31c   2.87300E-01

48116.31c   7.49000E-02

m9      13027.31c    1.0000E+00

1001.31c    1.7000E-01

mode n

*tr1  0 0 0   0 90 90 90 45 135 90 45 45

sdef erg=d1 pos 0 0 0 cel=60 rad=d2 ext=d3 axs 0 1 0

si1 0. 0.05 0.1 0.2 0.25 0.3 0.4 0.5 0.6 0.7 0.8

1.0 1.2 1.4 1.5 1.6 1.8 2.0 2.2 2.3 2.4 2.6 2.8 3.0

3.4 3.7 4.2 4.6 5.0 5.5 6.0 6.5 7.0 7.5 8.0 8.5

9.0 9.5 10. 11. 12. 13. 14. 16. 18.

sp1 0 0.0039 0.0074 0.0219 0.0140 0.0152 0.0323 0.0337 0.0343 0.0343

0.0338 0.0664 0.0641 0.0608 0.0290 0.0279 0.0527 0.0484

0.0442 0.0206 0.0196 0.0364 0.0328 0.0296 0.0503 0.0310

0.0413 0.0253 0.0200 0.0190 0.0140 0.0102 0.00734 0.00527

0.00378 0.00270 0.00193 0.00137 0.00098 0.00118 0.00059

0.00030 0.00015 0.00011 0.00003

si2 0 .1

si3 0.04

c

fc2  4-group reaction rates all 4 materials

f2:n (1 101) (2 102)

fs2 -1001

fm2 (1 101 -6)(1 102 -6) (1 103 -6) (1 104 -6)

e2 0.4e-6  0.4  1.4  20

tf2 1 1 j 1 1 j 1 j  $ 1st cell,total,j,1st seg,1st mult,j,1st energy

c

fc12  27-group reaction rates all 4 materials

f12:n (1 101) (2 102)

fs12 -1001

fm12 (1 101 -6)(1 102 -6) (1 103 -6) (1 104 -6)

e12 1.e-11 .01e-6 .03e-6 .05e-6 0.1e-6 0.225e-6 0.325e-6 0.4e-6 0.8e-6

1.e-6 1.13e-6 1.3e-6 1.77e-6 3.05e-6

1e-5 3e-5 1e-4 5.5e-4 3e-3 1.7e-2

.1 .4 .9 1.4 1.85 3.0 6.434 20

tf12 1 1 j 1 1 j 1 j  $ 1st cell,total,j,1st seg,1st mult,j,1st energy

c

fc22  plain flux

f22:n (1 101) (2 102)

fs22 -1001

e22 1e-8 1e-7 1e-6 1e-4 1e-2 1 18

tf22 1 1 j 1 1 j 1 j  $ 1st cell,total,j,1st seg,1st mult,j,1st energy

c

m101    92235.31c    1.0000E+00

m102    94239.31c    1.0000E+00

m103    92238.31c    1.0000E+00

m104    93237.31c    1.0000E+00

print

prdmp j -60

ctme 300

## F4. IPPE-FE

Fe#1 Shell R=4.5 r=2.0 (modeling of shell and n-source by S.Simakov)

C    -------- CELL CARDS ------------------

C    Fe - shell with cylinder hole

2    1    0.084018   (1 -2) #(1 -2 -41 -3)    imp:n=1

C    outside shell (void) + hole

c 3    0               (2 -5) :(1 -2 -4 -3)

C    ========== Target Assembly =======

C     :: TiT Target on Cu Radiator

11    3  -8.96 -40 41 -38                    imp:n=1

C     .. 1ST FLANGE + CONICAL TUBE + BOTTOM (ALUMINIUM)

12    4  -2.7  (-43 44 45 -46):(38 -39 -40 43):

(38 -39 -44 47):(-39 40 -42)  imp:n=1

C     .. 2ND FLANGE (EDEL STALL)

13    2  -7.9  (-47 48 49 -50)               imp:n=1

c    *** Outside target and shell ***

21    0         (-5)  #11 #12 #13 #2         imp:n=1

C     =============  Outside Welt ===========

100   0           5                          imp:n=0

C    ======     SURFACE CARDS ==================

C    -----  SPHERES AROUND ORIGIN ---------------

1    SO    2.0

2    SO    4.5

3    CX    2.0

c 4    PX    0.0

5    SO  680.0

C      =======  SURFACES For Target Assembly =======

c 35    SO       700.0

C     ** TIT TARGET

39    KX   8.381 0.0043066 -1

38    KX   7.598 0.0043066 -1

40    PX   0.1

41    PX   0.0

42    PX   0.15

C     ** 1st Al FLANGE/SCREW

43    PX  -2.8

44    PX  -3.5

45    CX   0.65

46    CX   1.15

C     ** 2nd SS FLANGE

47    PX  -32

48    PX  -32.7

49    CX    0.6

50    CX    2.65

C    ======== MATERIAL CARDS ================

C    Fe

M1      26054.31c    5.8900E-02

26056.31c    9.1520E-01

26057.31c    2.0900E-02

26058.31c    2.8000E-03

6000.31c    2.2000E-03

C     EDELSTAHL

M2      26056.31c   -6.9930E-01

28058.31c   -9.0000E-02

24052.31c   -1.8000E-01

25055.31c   -2.0000E-02

14028.31c  -9.22300E-03

14029.31c  -4.67000E-04

14030.31c  -3.10000E-04

6000.31c   -7.0000E-04

C      CUPPER

M3      29063.31c    6.9200E-01

29065.31c    3.0800E-01

C     ALUMINIUM

M4      13027.31c    1.0000E+00

C

MODE N

C      ======  Source ===============

SDEF  SUR=41 POS=0 0 0 RAD=D2 VEC=1 0 0 DIR=D3 ERG FDIR=D4

SI2  0.30

SI3  A -1.0000 -0.9962 -0.9848 -0.9659 -0.9397 -0.9063 -0.8660 -0.8192

-0.7660 -0.7071 -0.6428 -0.5736 -0.5000 -0.4226 -0.3420 -0.2588

-0.1737 -0.0872  0.0000  0.0872  0.1737  0.2588  0.3420  0.4226

0.5000  0.5736  0.6428  0.7071  0.7660  0.8192  0.8660  0.9063

0.9397  0.9659  0.9848  0.9962  1.0000

SP3     0.874   0.874   0.875   0.876   0.877   0.879   0.882   0.884

0.888   0.891   0.895   0.899   0.904   0.909   0.914   0.919

0.924   0.930   0.935   0.941   0.946   0.952   0.957   0.962

0.967   0.972   0.976   0.981   0.985   0.988   0.991   0.994

0.996   0.998   0.999   1.000   1.000

DS4     13.36   13.365  13.37   13.385  13.40   13.225  13.45   13.49

13.53   13.58   13.62   13.67   13.71   13.80   13.88   13.92

13.97   14.04   14.10   14.165  14.23   14.32   14.40   14.44

14.48   14.54   14.60   14.65   14.70   14.74   14.78   14.81

14.84   14.86   14.88   14.885  14.89

C    -------------------------------------------------------------------

C    CUT NEUTRON ENERGY RANGE

CUT:N 1J 1.0E-8  0.   0.

FC5   Ring (R=2.5) Detector at 679.0cm (175 bins)

F5X:N  679.0  2.5 0 ND

FM5    5.7936121E+06

E5                1.000E-07  4.140E-07  5.316E-07  6.826E-07  8.764E-07

1.125E-06  1.445E-06  1.855E-06  2.382E-06  3.059E-06  3.928E-06

5.044E-06  6.476E-06  8.315E-06  1.068E-05  1.371E-05  1.760E-05

2.260E-05  2.902E-05  3.727E-05  4.785E-05  6.144E-05  7.889E-05

1.013E-04  1.301E-04  1.670E-04  2.145E-04  2.754E-04  3.536E-04

4.540E-04  5.829E-04  7.485E-04  9.611E-04  1.234E-03  1.585E-03

2.035E-03  2.249E-03  2.485E-03  2.613E-03  2.747E-03  3.035E-03

3.355E-03  3.707E-03  4.307E-03  5.531E-03  7.102E-03  9.119E-03

1.060E-02  1.171E-02  1.503E-02  1.931E-02  2.188E-02  2.358E-02

2.418E-02  2.479E-02  2.606E-02  2.700E-02  2.850E-02  3.183E-02

3.431E-02  4.087E-02  4.631E-02  5.248E-02  5.656E-02  6.738E-02

7.200E-02  7.950E-02  8.250E-02  8.652E-02  9.804E-02  1.111E-01

1.168E-01  1.228E-01  1.291E-01  1.357E-01  1.426E-01  1.500E-01

1.576E-01  1.657E-01  1.742E-01  1.832E-01  1.926E-01  2.024E-01

2.128E-01  2.237E-01  2.352E-01  2.472E-01  2.732E-01  2.873E-01

2.945E-01  2.972E-01  2.985E-01  3.020E-01  3.337E-01  3.688E-01

3.877E-01  4.076E-01  4.505E-01  4.979E-01  5.234E-01  5.502E-01

5.784E-01  6.081E-01  6.393E-01  6.721E-01  7.065E-01  7.427E-01

7.808E-01  8.209E-01  8.629E-01  9.072E-01  9.616E-01  1.003E+00

1.108E+00  1.165E+00  1.225E+00  1.287E+00  1.353E+00  1.423E+00

1.496E+00  1.572E+00  1.653E+00  1.738E+00  1.827E+00  1.920E+00

2.019E+00  2.123E+00  2.231E+00  2.307E+00  2.346E+00  2.365E+00

2.385E+00  2.466E+00  2.592E+00  2.725E+00  2.865E+00  3.012E+00

3.166E+00  3.329E+00  3.679E+00  4.066E+00  4.493E+00  4.724E+00

4.966E+00  5.221E+00  5.488E+00  5.770E+00  6.065E+00  6.376E+00

6.592E+00  6.703E+00  7.047E+00  7.408E+00  7.788E+00  8.187E+00

8.607E+00  9.048E+00  9.512E+00  1.000E+01  1.051E+01  1.105E+01

1.162E+01  1.221E+01  1.252E+01  1.284E+01  1.350E+01  1.384E+01

14.0       14.1       14.2       14.3       14.4       14.5

14.6       14.65      14.70      14.75      14.80      14.81

14.82      14.83      14.84      14.85      14.86      14.87

14.88      14.89      14.90      14.91      14.92      14.93

14.94      14.95      14.96      14.97      14.98      14.99

15.00

PRINT

prdmp  -10000 -10000 1 5

c

NPS    1.E6

CTME   1000.

## F5. FNS_Oxygen

fns-tof/ lo2 slab-tof                 JENDL-3.2             '94-08-18

c    *****************************************************

c    *                  cell carad                       *

c    *****************************************************

c    ***************** external void *********************

1    0     -13 : +13 -2 +14 : +34 : +2 -34 +29 +30 +31 +32 +33

2    0           -21 -2 -19

c    ************** source vacuum region *****************

3    1 4.9210-5     -14 +13  -1 : -27  +1 -20

c    **************** naterial region ********************

c     ----sus316

4    2 8.5979-2  +1  -3 -14 +20 :  +4  -2 -14 +19 :  +3  -4 -14 +15

5    2 8.5979-2 +27 -28 -20     : +21 -22 -19

6    2 8.5979-2  +9 -11 -17 +20 : +12 -10 -17 +20 : +11 -12 -17 +18

7    2 8.5979-2 +25 -26 -20     : +23 -24 -20

c     ---- vacuum

8    0           +3  -5 -15 +20 :  +6  -4 -15 +19 :  +5  -6 -15 +16

9    0          +28  -5 -20     : +22  +6 -19

10    0           +7  -9 -17 +20 : +10  -8 -17 +20

11    0          +26  +7 -20     : +24  -8 -20

c     ---- al

12    3 3.6244-3   +5  -7 -16     :  +8  -6 -16     :  +7  -8 -16 +17

c     ---- o

13    4 4.2947-2 +11 -12 -18     : -25 -11 -20     : -23 +12 -20

c    ******* detector vacuum region *******

14    0  +2 -34 -29 : +2 -34 -30 : +2 -34 -31 : +2 -34 -32 : +2 -34 -33

c    ------- the following is a blank delimeter

c    **************************************

c    * surface card                       *

c    **************************************

1             pz          -28.0

2             pz            0.0

3             pz          -27.5

4             pz           -0.5

5             pz          -25.90

6             pz           -2.10

7             pz          -25.20

8             pz           -2.80

9             pz          -24.80

10             pz           -3.20

11             pz          -24.0

12             pz           -4.0

13             pz          -70.0

c     ------------------------------

14             cz           35.0

15             cz           34.7

16             cz           30.8

17             cz           30.0

18             cz           29.8

19             cz           23.25

20             cz           15.0

c     -----     test      ----------

21             sz           134.146   136.146

22             sz           134.096   136.146

23             sz          -105.7227  102.8227

24             sz          -105.6727  102.8227

25             sz            77.7227  102.8227

26             sz            77.6727  102.8227

27             sz          -129.7227  102.8227

28             sz          -129.6727  102.8227

c     21             pz            -0.05

c     22             pz            -0.10

c     23             sz        -105.7227  102.8227

c     24             sz        -105.6727  102.8227

c     25             pz           -24.05

c     26             pz           -24.10

c     27             sz        -129.7227  102.8227

c     28             sz        -129.6727  102.8227

c     ------------------------------

29             cz            4.977

30           1 cz            4.985

31           2 cz            5.012

32           3 cz            5.074

33           4 cz            5.212

34             so         1000.0

c     ------- the following is a blank delimeter

c    **************************************

c    *  mode card       - neutron only    *

c    **************************************

mode   n

c    **************************************

c    *  transformation cards              *

c    *  rotation about the y axis by theta*

c    **************************************

*tr1   0  0  0        12.2  90  102.2   90   0  90

77.8  90   12.2   +1

*tr2   0  0  0        24.9  90  114.9   90   0  90

65.1  90   24.9   +1

*tr3   0  0  0        41.8  90  131.8   90   0  90

48.2  90   41.8   +1

*tr4   0  0  0        66.8  90  156.8   90   0  90

23.2  90   66.8   +1

c    **************************************

c    *   cell parameter cards             *

c    **************************************

imp:n   0     1     1     1     1     1     1

1     1     1     1     1     1     1

c    ****************************************************

c    *  source specification cards                      *

c    *  src1=point isotropic option                     *

c    *  sdir dirc. biasing - height reduction considered*

c    *  si(eng.) and sp(prob.) taken from betof source  *

c    *  expt. data                                      *

c    ****************************************************

sdef  erg=d1  pos=0 0 -44.0  vec=0 0 1  dir=d2  wgt=1.0

sb2   -31   4.0

si1   4.0867-02  4.6308-02

5.2474-02  5.9461-02  6.7378-02  7.6349-02  8.6515-02

9.8035-02  1.1109-01  1.2588-01  1.4264-01  1.6163-01

1.8315-01  2.0754-01  2.3517-01  2.6649-01  3.0197-01

3.4217-01  3.8774-01  4.3936-01  4.9786-01  5.6415-01

6.3927-01  7.2438-01  8.2084-01  9.3013-01  1.0540+00

1.1943+00  1.3533+00  1.5335+00  1.7377+00  1.8498+00

1.9691+00  2.0961+00  2.2313+00  2.3752+00  2.5284+00

2.6914+00  2.8650+00  3.0498+00  3.2465+00  3.4559+00

3.6787+00  3.9160+00  4.1686+00  4.4374+00  4.7236+00

5.0282+00  5.3525+00  5.6978+00  6.0652+00  6.4564+00

6.8728+00  7.3161+00  7.7879+00  8.2902+00  8.8249+00

9.3940+00  9.9999+00  1.0157+01  1.0317+01  1.0480+01

1.0645+01  1.0812+01  1.0983+01  1.1156+01  1.1331+01

1.1510+01  1.1691+01  1.1875+01  1.2062+01  1.2252+01

1.2445+01  1.2641+01  1.2840+01  1.3042+01  1.3248+01

1.3456+01  1.3668+01  1.3883+01  1.4102+01  1.4324+01

1.4550+01  1.4779+01  1.5012+01  1.5248+01  1.5488+01

1.5732+01  1.5980+01  1.6231+01  1.6487+01

sp1   0          1.4214-04

2.1261-04  2.3162-04  2.1327-04  2.7087-04  2.6032-04

3.1949-04  3.7848-04  4.3099-04  4.4082-04  5.6289-04

6.0267-04  7.5334-04  8.3566-04  1.0281-03  1.1620-03

1.3881-03  1.5339-03  1.8001-03  2.0387-03  2.3534-03

2.6401-03  2.9843-03  3.2787-03  3.4783-03  3.7189-03

3.8514-03  4.0062-03  4.1197-03  1.9596-03  2.0343-03

2.0484-03  2.0263-03  1.9854-03  2.0112-03  2.0467-03

2.1441-03  2.2558-03  2.4800-03  2.0399-03  1.7933-03

1.6234-03  1.5383-03  1.4642-03  1.4261-03  1.3083-03

1.3177-03  1.1970-03  1.1469-03  1.0180-03  1.0084-03

1.0841-03  9.6395-04  9.2930-04  9.1702-04  1.1141-03

1.1989-03  3.0970-04  3.1532-04  3.2121-04  3.2516-04

3.9020-04  4.3484-04  4.3993-04  4.9814-04  5.7884-04

5.8531-04  7.1724-04  1.1255-03  1.1435-03  1.2050-03

2.3468-03  2.3827-03  2.4186-03  5.2339-03  5.8254-03

5.9374-03  2.4164-02  3.5089-02  3.5570-02  9.9593-02

1.8264-01  1.8583-01  1.6377-01  8.7669-02  8.9130-02

8.7095-02  1.0017-03  1.0217-03  0

c     *********************************************

c     *  material specification cards             *

c     *********************************************

c     ----- iron (fe) -----------------------------

c     --- air

m1    7014.31c 3.8810-5        8016.31c  1.0400-5

c     --- sus316: Cr=1.6787-2, Mn55=1.3420-3, Fe-6.0507-2, Ni=7.3429-3

m2   24050.31c 7.2940-4  24052.31c 1.4066-2  24053.31c 1.5948-3

24054.31c 3.9701-4

25055.31c 1.3420-3

26054.31c 3.5699-3  26056.31c 5.5497-2  26057.31c 1.2706-3

26058.31c 1.6942-4

28058.31c 5.0130-3  28060.31c 1.9165-3  28061.31c 8.2975-5

28062.31c 2.6361-4  28064.31c 6.6820-5

c     --- al

m3   13027.31c 3.6244-3

c     --- o

m4    8016.31c 4.2947-2

c     drxs

c    **********************************************

c    *  tally specification cards                 *

c    **********************************************

fc5  --//fluxes at 5 pt dts(th=0.0, 12.2, 24.9, 41.8, 66.8 deg)

f5:n        0.0         0     703.0000        1

148.7973      0     688.2148        1

298.0163      0     642.0212        1

477.4981      0     534.0526        1

676.2307      0     289.8328        1

dd    0.5   100

e0    4.0867-02  4.6308-02

5.2474-02  5.9461-02  6.7378-02  7.6349-02  8.6515-02

9.8035-02  1.1109-01  1.2588-01  1.4264-01  1.6163-01

1.8315-01  2.0754-01  2.3517-01  2.6649-01  3.0197-01

3.4217-01  3.8774-01  4.3936-01  4.9786-01  5.6415-01

6.3927-01  7.2438-01  8.2084-01  9.3013-01  1.0540+00

1.1943+00  1.3533+00  1.5335+00  1.7377+00  1.8498+00

1.9691+00  2.0961+00  2.2313+00  2.3752+00  2.5284+00

2.6914+00  2.8650+00  3.0498+00  3.2465+00  3.4559+00

3.6787+00  3.9160+00  4.1686+00  4.4374+00  4.7236+00

5.0282+00  5.3525+00  5.6978+00  6.0652+00  6.4564+00

6.8728+00  7.3161+00  7.7879+00  8.2902+00  8.8249+00

9.3940+00  9.9999+00  1.0157+01  1.0317+01  1.0480+01

1.0645+01  1.0812+01  1.0983+01  1.1156+01  1.1331+01

1.1510+01  1.1691+01  1.1875+01  1.2062+01  1.2252+01

1.2445+01  1.2641+01  1.2840+01  1.3042+01  1.3248+01

1.3456+01  1.3668+01  1.3883+01  1.4102+01  1.4324+01

1.4550+01  1.4779+01  1.5012+01  1.5248+01  1.5488+01

1.5732+01  1.5980+01  1.6231+01  1.6487+01

fq0    e    f

c    ***********************************************

c    * problem cutoff cards                        *

c    ***********************************************

cut:n        0     4.0000-02   -10    -0.01

nps      2000000

c ctme      180

c    ***********************************************

c    * peripheral crads                            *

c    ***********************************************

prdmp      1000000    1000000

lost     10        10

print

## F6. Oktavian Al

LEAKAGE FROM ALUMINIUM (40 CM DIA) SPHERE 3-D SURFACE TALLY (ENDF/B-VI)

c    *** Cell cards ***

1     3  -0.0012  -3

2     2  -7.824   -4 3

3     1  -1.223   -5 4

4     2  -7.824   -6 5

5     3  -0.0012  -7 6

6     0            7

c    *** Surface cards ***

3    so  10.0

4    so  10.2

5    so  19.75

6    so  19.95

7    so 580.0

c    *** Material cards ***

c Aluminium (0.2% Fe-56, ignore Si, Cu)

m1      13027.31c   -9.9800E-01

26056.31c   -2.0000E-03

c Steel (Cr 18.5%, Fe-56 70.4%, Ni 11.1%)

m2    24050.31c  -8.03825E-03

24052.31c  -1.55010E-01

24053.31c  -1.75768E-02

24054.31c  -4.37525E-03

26056.31c   -7.0400E-01

28058.31c  -7.55655E-02

28060.31c  -2.91075E-02

28061.31c  -1.26540E-03

28062.31c  -4.03374E-03

28064.31c  -1.02786E-03

c  Air

m3    8016.31c  0.208

7014.31c  0.792

c    *** Data cards ***

mode n

imp:n 1 1 1 1 1 0

sdef pos=0. 0. 0. cel=1 erg=d1

c    *** Energy bin for source neutron ***

si1  h 1.000e-1 1.120e-1 1.260e-1 1.410e-1 1.590e-1

1.780e-1 2.000e-1 2.240e-1 2.520e-1 2.830e-1

3.170e-1 3.560e-1 4.000e-1 4.490e-1 5.040e-1

5.660e-1 6.350e-1 7.130e-1 8.000e-1 8.780e-1

9.640e-1 1.058e+0 1.162e+0 1.275e+0 1.400e+0

1.542e+0 1.698e+0 1.871e+0 2.061e+0 2.270e+0

2.500e+0 2.704e+0 2.924e+0 3.162e+0 3.419e+0

3.699e+0 4.000e+0 4.165e+0 4.337e+0 4.516e+0

4.703e+0 4.897e+0 5.099e+0 5.310e+0 5.529e+0

5.757e+0 5.995e+0 6.242e+0 6.500e+0 6.765e+0

7.041e+0 7.327e+0 7.627e+0 7.938e+0 8.261e+0

8.598e+0 8.949e+0 9.314e+0 9.693e+0 1.009e+1

1.050e+1 1.082e+1 1.114e+1 1.148e+1 1.183e+1

1.218e+1 1.255e+1 1.277e+1 1.300e+1 1.324e+1

1.348e+1 1.372e+1 1.397e+1 1.422e+1 1.447e+1

1.474e+1 1.500e+1 1.527e+1 1.554e+1 1.583e+1

1.611e+1 1.640e+1

c    *** Source distribution ***

sp1    0.000e-4 0.000e-0 0.000e-0 1.270e-4 5.774e-5

2.536e-4 2.722e-4 2.076e-4 4.366e-4 3.873e-4

4.756e-4 6.161e-4 6.727e-4 6.648e-4 8.581e-4

1.098e-3 1.184e-3 1.412e-3 1.616e-3 1.546e-3

1.556e-3 1.631e-3 1.771e-3 1.804e-3 1.823e-3

1.891e-3 1.935e-3 2.002e-3 2.052e-3 2.004e-3

2.068e-3 2.091e-3 3.354e-3 1.492e-3 1.322e-3

1.451e-3 1.401e-3 7.112e-4 6.423e-4 6.514e-4

6.195e-4 6.428e-4 6.209e-4 5.788e-4 5.227e-4

5.250e-4 5.456e-4 5.106e-4 5.789e-4 5.391e-4

4.998e-4 4.813e-4 5.300e-4 5.756e-4 5.230e-4

5.394e-4 6.256e-4 7.047e-4 7.729e-4 7.951e-4

8.659e-4 8.106e-4 8.923e-4 1.022e-3 1.281e-3

1.687e-3 2.286e-3 1.825e-3 2.479e-3 3.794e-3

7.010e-3 1.565e-2 3.634e-2 7.492e-2 1.279e-1

1.768e-1 1.916e-1 1.500e-1 8.676e-2 3.950e-2

1.430e-2 4.269e-3

c    *** Tally cards ***

fc21 Neutron current through the outer surface

f21:n 7

c    *** Energy bin ***

e21           1.290e-3 1.670e-3 2.150e-3

2.780e-3 3.590e-3 4.640e-3 5.990e-3 7.740e-3

1.000e-2 1.290e-2 1.670e-2 2.150e-2 2.780e-2

3.590e-2 4.640e-2 5.990e-2 7.740e-2

1.000e-1 1.060e-1 1.120e-1 1.190e-1

1.260e-1 1.340e-1 1.410e-1 1.500e-1 1.590e-1

1.680e-1 1.780e-1 1.890e-1 2.000e-1 2.120e-1

2.240e-1 2.520e-1 2.830e-1 3.170e-1 3.560e-1

4.000e-1 4.490e-1 5.040e-1 5.660e-1 6.350e-1

7.130e-1 8.000e-1 8.780e-1 9.640e-1 1.058e+0

1.162e+0 1.275e+0 1.400e+0 1.542e+0 1.698e+0

1.871e+0 2.061e+0 2.270e+0 2.500e+0 2.704e+0

2.924e+0 3.162e+0 3.419e+0 3.699e+0 4.000e+0

4.165e+0 4.337e+0 4.516e+0 4.703e+0 4.897e+0

5.099e+0 5.310e+0 5.529e+0 5.757e+0 5.995e+0

6.242e+0 6.500e+0 6.765e+0 7.041e+0 7.327e+0

7.627e+0 7.938e+0 8.261e+0 8.598e+0 8.949e+0

9.314e+0 9.693e+0 1.009e+1 1.050e+1 1.082e+1

1.114e+1 1.148e+1 1.183e+1 1.218e+1 1.255e+1

1.277e+1 1.300e+1 1.324e+1 1.348e+1 1.372e+1

1.397e+1 1.422e+1 1.447e+1 1.474e+1 1.500e+1

1.527e+1 1.554e+1 1.583e+1 1.611e+1 1.640e+1

fc32 Photon current through the outer surface

f32:p 7

fm32 4227327.1             $ 4*Pi * R7

fq32 e t

c    *** Energy bin ***

e32  0.3  56i  6.0  19i  10.0  24i  20

t32  8.8  1e6  t

c

phys:n 20.0  0

phys:p 20.0  0  0

phys:e 20.0  0  0  0  0  1  0  1  1

c    *** Cut off card ***

c cut:n 1.0e16 1.0e-3 0.01

cut:n 1.0e6  0.0    -0.5  -0.25  0

cut:p 1.0e6  0.299  -0.5  -0.25  0

cut:e 1.0e6  0.3    -0.5  -0.25  0

c    *** Neutron history ***

nps  5000000

print

## F7. LLNL Pulsed Spheres: Iron, 4.8 MFP

IRON SPHERE WITH 4.8 M.F.P ENDF/B-VI AND JEFF-3.1

1 1 -7.85    -1 -3

2 1 -7.85     1  2 -3

3 2 -.001288  1 -2 -3

4 1 -7.85    -1  3 -4

5 1 -7.85     1  2  3 -4

6 2 -.001288  1 -2  3 -4

7 1 -7.85    -1  4 -5

8 1 -7.85     1  2  4 -5

9 2 -.001288  1 -2  4 -5

10 1 -7.85   -1  5 -6

11 1 -7.85    1  2  5 -6

12 2 -.001288 1 -2 5 -6

13 2 -.001288 6 -7

14 0 7

1   px -.475

2   x 0.0 1.11 22.3 2.67

3   so 6

4   so 12

5   so 18

6   so 22.3

7   so 1000

100 px 0.0

IMP:N 1 1 1 2 2 2 4 4 4 8 8 8 8 0

c data cards - source (as given by LA-12212 and LA-12885)

sdef pos=0 0 0 dir=d1 erg=fdir=d2 rad=d3 vec=-1 0 0

sur=100 tme=d4

si1 a -1.00000 -0.99619 -0.98481 -0.96593 -0.93969

-0.90631 -0.86603 -0.81915 -0.76604 -0.70711

-0.64279 -0.57358 -0.50000 -0.42262 -0.34202

-0.25882 -0.17365 -0.08716  0.00000  0.08716

0.17365  0.25882  0.34202  0.42262  0.50000

0.57358  0.64279  0.70711  0.76604  0.81915

0.86603  0.90631  0.93969  0.96593  0.98481

0.99519 1.00000

sp1    0.874 0.874 0.875 0.876 0.877

0.879 0.882 0.884 0.888 0.891

0.895 0.899 0.904 0.909 0.914

0.919 0.924 0.930 0.935 0.941

0.946 0.952 0.957 0.962 0.967

0.972 0.976 0.981 0.985 0.988

0.991 0.994 0.996 0.998 0.999

1.000 1.000

ds2 q  -0.99619 180 -0.98481 175 -0.96593 170 -0.93962 165

-0.90631 160 -0.86603 155 -0.81915 150 -0.76604 145

-0.70711 140 -0.64279 135 -0.57358 130 -0.50000 125

-0.42262 120 -0.34202 115 -0.25882 110 -0.17365 105

-0.08716 100 0.00000 95 0.08716 90 0.17365 85

0.25882 80 0.34202 75 0.42262 70 0.50000 65

0.57358 60 0.64279 55 0.70711 50 0.76604 45

0.81915 40 0.86603 35 0.90631 30 0.93969 25

0.96593 20 0.98481 15 0.98619 10 1.00000 5

si3 h  0 0.6

sp3 d -21 1

sp4 -41 .3 0

si5 h 15.106 15.110

sp5 d 0 1

si10 h 15.095 15.106

sp10 d 0 1

si15 h 15.075 15.095

SP15 d 0 1

si20 h 15.049 15.075

sp20 d 0 1

si25 h 15.015 15.049

sp25 d 0 1

si30 h 14.974 15.015

sp30 d 0 1

si35 h 14.927 14.974

sp35 d 0 1

si40 h 14.873 14.927

SP40 d 0 1

si45 h 14.814 14.873

sp45 d 0 1

si50 h 14.750 14.814

sp50 d 0 1

si55 h 14.681 14.750

sp55 d 0 1

si60 h 14.608 14.681

sp60 d 0 1

si65 h 14.532 14.608

sp65 d 0 1

si70 h 14.453 14.532

sp70 d 0 1

si75 h 14.372 14.453

sp75 d 0 1

si80 h 14.289 14.372

sp80 d 0 1

si85 h 14.206 14.289

sp85 d 0 1

si90 h 14.123 14.206

sp90 d 0 1

si95 h 14.040 14.123

sp95 d 0 1

si100 h 13.958 14.040

sp100 d 0 1

si105 h 13.878 13.958

sp105 d 0 1

si110 h 13.800 13.878

sp110 d 0 1

si115 h 13.725 13.800

sp115 d 0 1

si120 h 13.654 13.725

sp120 d 0 1

si125 h 13.586 13.654

sp125 d 0 1

si130 h 13.522 13.586

sp130 d 0 1

si135 h 13.464 13.522

sp135 d 0 1

si140 h 13.410 13.464

sp140 d 0 1

si145 h 13.362 13.410

sp145 d 0 1

si150 h 13.320 13.362

sp150 d 0 1

si155 h 13.284 13.320

sp155 d 0 1

si160 h 13.254 13.284

sp160 d 0 1

si165 h 13.230 13.254

sp165 d 0 1

si170 h 13.214 13.230

sp170 d 0 1

si175 h 13.203 13.214

sp175 d 0 1

si180 h 13.200 13.203

sp180 d 0 1

FC5 NE213 DETECTOR RESPONSE FUNCTION, 766CM FLIGHTPATH, 30 DEGREES

f5x:n -663.4 383 0.0

t5   1.37E+01 1.39E+01 1.41E+01 1.43E+01 1.45E+01 1.47E+01

1.49E+01 1.51E+01 1.53E+01 1.55E+01 1.57E+01 1.59E+01

1.61E+01 1.63E+01 1.65E+01 1.67E+01 1.69E+01 1.71E+01

1.73E+01 1.75E+01 1.77E+01 1.79E+01 1.81E+01 1.83E+01

1.85E+01 1.87E+01 1.89E+01 1.91E+01 1.93E+01 1.95E+01

1.97E+01 1.99E+01 2.01E+01 2.03E+01 2.05E+01 2.07E+01

2.09E+01 2.11E+01 2.13E+01 2.15E+01 2.17E+01 2.19E+01

2.21E+01 2.23E+01 2.25E+01 2.27E+01 2.29E+01 2.31E+01

2.33E+01 2.35E+01 2.37E+01 2.39E+01 2.41E+01 2.43E+01

2.45E+01 2.47E+01 2.49E+01 2.51E+01 2.53E+01 2.55E+01

2.57E+01 2.59E+01 2.61E+01 2.63E+01 2.65E+01 2.67E+01

2.69E+01 2.71E+01 2.73E+01 2.75E+01 2.77E+01 2.79E+01

2.81E+01 2.83E+01 2.85E+01 2.87E+01 2.89E+01 2.91E+01

2.93E+01 2.95E+01 2.97E+01 2.99E+01 3.01E+01 3.03E+01

3.05E+01 3.07E+01 3.09E+01 3.11E+01 3.13E+01 3.15E+01

3.17E+01 3.19E+01 3.21E+01 3.23E+01 3.25E+01 3.27E+01

3.29E+01 3.31E+01 3.33E+01 3.35E+01 3.37E+01 3.39E+01

3.41E+01 3.43E+01 3.45E+01 3.47E+01 3.49E+01 3.51E+01

3.53E+01 3.55E+01 3.57E+01 3.59E+01 3.61E+01 3.63E+01

3.65E+01 3.67E+01 3.69E+01 3.71E+01 3.73E+01 3.75E+01

3.77E+01 3.79E+01 3.81E+01 3.83E+01 3.85E+01 3.87E+01

3.89E+01 3.91E+01 3.93E+01 3.95E+01 3.97E+01 3.99E+01

4.01E+01 4.03E+01 4.05E+01 4.07E+01 4.09E+01 4.11E+01

4.13E+01 4.15E+01 4.17E+01

c ne213 low bias response function

de5 lin 1.6 1.8 1.9 2.0 2.1 2.2 2.3 2.4 2.5 2.75

3.0 3.5 4.0 4.5 5.0 5.5 6.0 6.4 6.6 6.8 7.0

7.5 8.1 8.5 9.0 10.0 11.0 12.0 12.5 13.0

13.5 14.0 15.0 16.0

df5 lin 0.00 1.46 1.86 2.26 2.58 3.00 3.29 3.42

3.63 3.95 4.10 4.25 4.33 4.39 4.40 4.37 4.28

4.15 4.20 4.18 4.12 3.97 3.80 3.77 3.65 3.44

3.24 3.06 3.01 2.98 2.98 3.01 3.08 3.25

M1   26054.31c .0562600

26056.31c .8896840

26057.31c .0213400

26058.31c .0027160

6000.31c .012

25055.31c .010

15031.31c .007

16032.31c .001

M2    7014.31c -.7885

8016.31c -.2115

CUT:N 39.1 1.6

PRINT

prdmp 2j -1

nps 20000000

# Text boxes

C--------------------------------------------------------------------

C

C     USE LOG-LOG INTERPOLATION AT LOW ENERGY

C

C--------------------------------------------------------------------

ITERP=2

C-----02/03/00 - ADD LOG-LOG ONLY IF CROSS SECTIONS > 0

IF(XCIN(IFILL).GT.0.0.AND.XCKM1.GT.0.0.AND.

1   ALPHA*ENEXT.LE.4.0D+01) ITERP=5

XCCOLD(K)=TERPIT(ENEXT,EIN(IFILL),EKM1,XCIN(IFILL),XCKM1,ITERP)

ARG=ALPHA*ECOLD(K)

YCOLD(K)=DSQRT(ARG)

GO TO 320

*  Beryllium     - Thermal Neutron Scattering Law Data in MF=7   *  26 1451   17

*                  T=293.6 400 500 600 700 800 1000 1200 K       *  26 1451   19

Graphite  IKE        EVAL-JAN05 Keinert, Mattes                    31 1451    5

* Temperatures (K) = 293.6, 400, 500, 600, 700, 800, 1000,       *  31 1451   17

*                   1200, 1600, 2000, 3000                       *  31 1451   18

D(D2O)    IKE        EVAL-FEB04 Keinert,Mattes                     11 1451    5

*Temperatures: 293.6 323.6 373.6 423.6 473.6 523.6 573.6 643.9 K *  11 1451   17

H(ZrH)    IKE        EVAL-JAN05 Keinert                             7 1451    5

*  TEMPERATURES = 293.6 400 500 600 700 800 1000 1200 DEG K.    *   7 1451   16

H(H2O)    IKE        EVAL-JAN04 Keinert,Mattes                      1 1451    5

* Temperatures (K)= 293.6  323.6  373.6  423.6  473 .6 523.6     *   1 1451   17

*                   573.6  623.6  647.2  800   1000              *   1 1451   18

*  Polyethylene  - Thermal Neutron Scattering Law Data in MF=7   *  37 1451   22

*  H (CH2)              are given for the temperatures           *  37 1451   23

*                                    T= 293.6 and 350 K          *  37 1451   24

moder / Extract thermal Scattering Law

1 -61

' H-CH2    from JEFF3.1'/

60 37

0/

moder / Extract/convert neutron evaluated data

1 -21

'1-H-1 from JEFF3.1'/

20 125

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 1-H-1'/

125 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 1-H-1 from JEFF3.1'/

'Processed by NJOY99.90+NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

125 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

293.6

0/

thermr / Add thermal scattering data (free gas)

0 -23 -62

0 125 12 1 1 11 1 221 1/ MATDE MATDP NBIN NTEMP IINC ICOH NATOM MTREF IPRINT

293.6

0.001 5.0

thermr / Add thermal scattering data (bound)

-61 -62 -27

37 125 16 1 4 11 2 223 1/MATDE MATDP NBIN NTEMP IINC ICOH NATOM MTREF IPRINT

293.6

0.001 5.0

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/ IOPT IPRINT NTYPE SUFF

'H-CH2   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 293.6 'poly01' / MATD TEMPD TNAME

1001    0    0 / IZA01 IZA02 IZA03

223 64 224  1  1 4.0 0/ MTI NBINT MTE IELAS NMIX EMAX IWT

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

stop

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/ IOPT IPRINT NTYPE SUFF

'H-CH2   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 293.6 'poly01' / MATD TEMPD TNAME

1001    0    0 / IZA01 IZA02 IZA03

223 64 224  1  1 4.0 0/ MTI NBINT MTE IELAS NMIX EMAX IWT

acer / Check ACE files

0 28 0 71 81

7 1 1 -1/

/

xsdir_ascii  xsdir_bin

jeff31_ascii jeff31_bin 2

datapath=.

atomic weight ratios

0001  1.000000      0001  1.000000

1000  0.99931697    1001  0.99916732   1002  1.99679966   1003  2.99013994

2000  3.96821760    2003  2.99012015   2004  3.96821894

3000  6.88131188    3006  5.96344945   3007  6.95573316

4000  8.93476310    4007  6.95665041   4009  8.93476310

…

…

99000  251.818000    99240  238.006611   99241  238.997765   99242  239.990202

99243  240.981544   99244  241.974280   99245  242.966035

99246  243.959078   99247  244.951167   99248  245.944369

99249  246.936717   99250  247.930357   99251  248.923084

99252  249.917457   99253  250.910696   99254  251.905276

99255  252.898917   99256  253.893623   99257  254.887399

100000  252.899000   100255  252.899000

02/03/2000

directory

1001.31c    0.999170       H1.ACE 0 1   1   10161     0     0 2.585E-08

1002.31c    1.996800       H2.ACE 0 1   1   10882     0     0 2.585E-08

1003.31c    2.990140       H3.ACE 0 1   1    7320     0     0 2.585E-08

2003.31c    2.989032      He3.ACE 0 1   1    9680     0     0 2.585E-08

2004.31c    3.968200      He4.ACE 0 1   1   26134     0     0 2.585E-08

…

…

99253.31c  250.910000    Es253.ACE 0 1   1   64848     0     0 2.585E-08 ptable

99254.31c  251.905000    Es254.ACE 0 1   1   38692     0     0 2.585E-08

99255.31c  252.899000    Es255.ACE 0 1   1   19107     0     0 2.585E-08

100255.31c  252.899000    Fm255.ACE 0 1   1   17459     0     0 2.585E-08

xsdir xsdir_ascii

jeff31_ascii           1

1001.31c

1002.31c

…

…

99255.31c

100255.31c

REM -------

REM --- Isotopes to build library in: specs_type1

REM --- Update: xsdir_type1 with .dir files

REM -------------------

copy  specs_type1     specs

copy  xsdir_type1	xsdir

makxsf.exe

move tprint tprint_ascii

copy specs_type2 	specs

makxsf.exe

move tprint tprint_bin

REM - Build Updated NJOY for JEFF31 (November 2005)

del *.f

copy upn90_noup63_noup56+uplf95+upn_Leichtle_Mod+upn_Sublet+upn_Aldama+upn_Mattes+upn_Trkov+upn_Ads+upn_Cad+upn_Shimizu+upn_Pescarini+upn_Cabellos+upn_Hogenbirk upn

upd.exe

REM -----

REM upn90_noup63_noup56 : (included in upn_Hogenbirk)

REM                  - Include upn90 except for:

REM                  - up63 to treat delayed neutrons (updated in upn_Hogenbirk)

REM                  - up64, up72 and up75 do not include updates for up63

REM                  - up56: converting law7 into law1

REM                  - up64 does not include update for up56

REM

REM uplf95       : for lahey95

REM upn_Trkov    : IAEA upn for fendl2.1

REM       - Include: upiaea1, upijs57,upijs59, upijs61, upijs62, upijs63, upijs64

REM         upiaea2 upiaea3, upfendl1,upfndl2, upfndl3, upfndl4, upfndl5, upfndl6

REM upn_Mattes   : Thermal Scattering Libraries

REM   - Include:  up3_thermr, up1_leapr, up2_leapr, up3_leapr, up4_leapr,

REM               up5_leapr, up_acer

REM                  Modifications in common/xsst/

REM                - Do not include: up_thermr (updated in upn_Aldama)

REM upn_Aldama   : up_therm1 update included in upn_Mattes (included in upn_ADS)

REM upn_Hogenbirk: Delayed neutrons in ACE format for JEFF31.

REM               - Include: nrg_a50, nrg_a52, nrg_a57, nrg_re15 (dla1 in upn_ADS)

REM upn_Sublet   : upki (included in upn_Hogenbirk)

REM upn_ADS      :

REM                  - Include: ads01, ads02, ads03

REM                  - Do not include:

REM                1) upiaea1, upijs57, upijs59, upijs61, upijs62, upijs63, upijs64

REM                   upiaea2 upiaea3, upfendl1, upfndl2, upfndl3, upfndl4,

REM                   upfndl5, upfndl6: included in upn_Trkov

REM                2) wlup2: included in upn_Aldama

REM                3) up3_thermr, up1_leapr, up2_leapr, up3_leapr, up4_leapr,

REM                   up5_leapr, up_acer : included in upn_Mattes

REM                4) upshim: included in upn_Shimizu

REM                5) upcad: included in upn_CAD

REM upn_CAD      : upcad (included in ADS)

REM upn_Shimizu  : upshim (included in ADS)

REM upn_Cabellos : JEFF31 update

REM                -llf

REM upn_Leichtle_Mod : Be-9 and others (Li7)

REM                - Include: upac1, upac2 (with some modifications because it

REM                  corresponds with up57)

REM                - Do not include:

REM                  - upre1 (equivalent to up54)

REM                  - upac3 (equivalent to up57)

REM upn_Pescarini: JEFF31 corrections.

REM              - Does not include updates equivalents to upfndl2, upki,

REM                up_thermr,nrg_re15

REM -----

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .31/

'89-Ac-225 from JEFF3.1(JEFF3.1) NJOY 99.90 NEA Oct2005'/

8925 300.

1 1/

/

acer / Check ACE files

0 27 0 29 30

7 1 1 -1/

/

purr / Process Unresolved Resonance Range if any

-21 -41 -26

8925 1 1 20 100/ matd ntemp nsigz nbin nladr

300.

1.E+10

0/

thermr / Add thermal scattering data

0 -25 -41

0 8925 12 1 1 0 1 221 1/ MATDE MATDP NBIN NTEMP IINC ICOH NATOM MTREF IPRINT

300.

0.001 4.0

gaspr / Add gas production

-21 -24 -25

heatr / Add heating kerma and damage energy

-21 -23 -24/

8925 7 0 0 0 2/

302 303 304 318 402 443 444/

broadr / Doppler broaden XS

-21 -22 -23

8925 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

300.

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 89-Ac-225'/

8925 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 89-Ac-225 from JEFF3.1'/

'Processed by NJOY-99.90 at NEA Oct2005'/

0/

moder / Extract/convert neutron evaluated data

1 -21

'89-Ac-225 from JEFF3.1'/

20 8925

0/

reconr / Reconstruct XS for neutrons

-21 -22

'JEFF3.1 PENDF for 89-Ac-225'/

8925 2/

0.001 0. 0.003/ err tempr errmax

'JEFF3.1: 89-Ac-225 from JEFF3.1'/

'Processed by NJOY-99.90 at NEA Oct2005'/

0/

broadr / Doppler broaden XS

-21 -22 -23

8925 1 0 0 0./

0.001 2.0e6 0.003/ errthn thnmax errmax

300.

0/

heatr / Add heating kerma and damage energy

-21 -23 -24/

8925 7 0 0 0 2/

302 303 304 318 402 443 444/

gaspr / Add gas production

-21 -24 -25

thermr / Add thermal scattering data

0 -25 -41

0 8925 12 1 1 0 1 221 1/

300.

0.001 4.0

purr / Process Unresolved Resonance Range if any

-21 -41 -26

8925 1 1 20 100/ matd ntemp nsigz nbin nladr

300.

1.E+10

0/

acer / Prepare ACE files

-21 -26 0 27 28

1 0 1 .31/

'89-Ac-225 from JEFF3.1(JEFF3.1) NJOY 99.90 NEA Oct2005'/

8925 300.

1 1/

/

acer / Check ACE files

0 27 0 29 30

7 1 1 -1/

/

stop

del *.f

REM ----

copy up112+uplf95+upn_pescarini+upn_cabellos upn

upd.exe

FE56

-------

heatr

---message from sixbar---no distribution for mt  5 particle **

---message from h6ddx---vertical segment(s) in distribution

purr

---message from purr---mat 2631 has no unresolved parameters

acer checking

---message from consis---consistency problems found

----------------------------------------------------

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-CH2   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 293.6 'poly01' /

1001    0    0 /

223 64 224  1  1 4.0 0/

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-H2O   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 293.6 'lwtr01' /

1001    0    0 /

222 64   0  0  1 4.0 0/

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'H-ZrH   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

125 293.6 'hzrh01' /

1001    0    0 /

225 64 226  1  1 4.0 0/

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'D-D2O   293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

128 293.6 'hwtr01' /

1002    0    0 /

228 64   0  0  1 4.0 0/

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'4-Be    293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

425 293.6 'beo01 ' /

4009 8016    0 /

233 64 234  0  2 4.0 0/

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'4-Be    293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

425 293.6 'bena01' /

4009    0    0 /

231 64 232  0  1 4.0 0/

MODER

RECONRR

BROADR

HEATR

GASPR

THERMR

ACER

(Check ACE file)

ACER

(Create ACE file)

PURR

acer / Prepare ACE files

-21 -27 0 28 29

2 0 1 .31/

'Graphi  293.6 K from (JEFF3.1) NJOY99.90+NEA Oct2005'/

600 293.6 'grph01' /

6000    0    0 /

229 64 230  0  1 4.0 0/

moder / Extract/convert neutron evaluated data

1 -21

'89-Ac-225 from JEFF3.1'/

20 8925

0/

MAKXSF

SPEC file

XSDIR file

XS libraries (*.ACE)

TPRINT (error file)

New XSDIR file

XS Library

ace consistency checks

----------------------

check reaction thresholds against q values

check that main energy grid is monotonic

check angular distributions for correct reference frame

check angular distributions for unreasonable cosine values

check energy distributions

check photon production sum

check photon distributions

checking particle production sections

deuteron production

checking energy distributions

e= 9.8400E+02   spot= 4.9845E+00   dbar= 2.4262E+00   sigx= 1.3423E-07

total     elastic     fission     capture

1  1.3139E+01  8.6874E+00  0.0000E+00  4.4517E+00

2  1.4419E+01  9.4455E+00  0.0000E+00  4.9735E+00

3  1.4322E+01  9.3227E+00  0.0000E+00  4.9995E+00

...

...

97  1.3283E+01  8.9758E+00  0.0000E+00  4.3068E+00

98  1.5700E+01  1.0444E+01  0.0000E+00  5.2565E+00

99  1.3695E+01  9.1265E+00  0.0000E+00  4.5688E+00

100  1.4433E+01  9.4805E+00  0.0000E+00  4.9528E+00

bkgd -2.4793E-01  2.6408E-02  0.0000E+00 -2.7434E-01

infd  1.3695E+01  9.0847E+00  0.0000E+00  4.6105E+00

aver  1.3578E+01  9.0208E+00  0.0000E+00  4.5573E+00

pcsd        5.15        4.99        0.00        6.26

nres        3315

bondarenko cross sections by direct sampling

temp      sig0    p0 total     elastic     fission     capture    p1 total

3.000E+02 1.000E+10  1.3578E+01  9.0208E+00  0.0000E+00  4.5573E+00  1.3578E+01

probability table

tmax 3.00E+02 2.48E+00 3.31E+00 4.06E+00  4.32E+00   4.55E+00   4.71E+00   4.81E+00   4.95E+00  5.15E+00 5.38E+00

5.66E+00 6.04E+00 6.62E+00  7.60E+00   9.19E+00   1.28E+01   2.72E+01   1.06E+02  2.05E+02 5.77E+02

prob 3.00E+02 3.61E-03 1.82E-02 6.15E-02  4.91E-02   6.31E-02   6.31E-02   5.80E-02   5.53E-02  6.41E-02 6.18E-02

5.69E-02 5.75E-02 6.18E-02  6.22E-02   5.55E-02   5.84E-02   6.41E-02   6.25E-02  1.55E-02 6.97E-03

tot  3.00E+02 2.15E+00 2.99E+00 3.76E+00  4.19E+00   4.44E+00   4.63E+00   4.76E+00   4.88E+00  5.04E+00 5.26E+00

5.51E+00 5.84E+00 6.31E+00  7.06E+00   8.30E+00   1.07E+01   1.82E+01   5.44E+01  1.43E+02 2.78E+02

els  3.00E+02 1.65E+00 2.70E+00 3.69E+00  4.22E+00   4.51E+00   4.74E+00   4.90E+00   4.96E+00  5.06E+00 5.19E+00

5.33E+00 5.48E+00 5.67E+00  5.92E+00   6.27E+00   6.92E+00   9.13E+00   2.47E+01  8.01E+01 1.82E+02

fis  3.00E+02 0.00E+00 0.00E+00 0.00E+00  0.00E+00   0.00E+00   0.00E+00   0.00E+00   0.00E+00  0.00E+00 0.00E+00

0.00E+00 0.00E+00 0.00E+00  0.00E+00   0.00E+00   0.00E+00   0.00E+00   0.00E+00  0.00E+00 0.00E+00

cap  3.00E+02 5.00E-01 2.96E-01 7.19E-02 -2.805E-02 -7.634E-02 -1.096E-01 -1.375E-01 -8.33E-02 -2.07E-02 7.13E-02

1.86E-01 3.52E-01 6.40E-01  1.145E+00  2.039E+00  3.791E+00  9.097E+00  2.97E+01  6.32E+01 9.58E+01

bondarenko cross sections from probability table

temp      sig0    p0 total     elastic     fission     capture    p1 total

3.000E+02 1.000E+10  1.3578E+01  9.0208E+00  0.0000E+00  4.5573E+00  1.3578E+01

11-Na-22	18-Ar-36	44-Ru-101	46-Pd-104	46-Pd-106

46-Pd-107	46-Pd-108 	46-Pd-110	47-Ag-109	57-La-139

59-Pr-141	60-Nd-144	60-Nd-145	60-Nd-146	60-Nd-148

61-Pm-147	93-Np-238	88-Cf-252	99-Es-253

8.100000+4 2.026300+2          0          0          0          08100 3102 1077

6.655800+6 6.655800+6          0          0          1         678100 3102 1078

67          2                                            8100 3102 1079

1.000000-5 1.200000+2 2.530000-2 3.430000+0 7.000000-1 8.000000-18100 3102 1080

1.250000+0 6.500000-1 1.950000+0 5.500000-1 3.450000+0 3.700000-18100 3102 1081

8.450000+0 2.500000-1 1.310000+1 1.950000-1 1.620000+1 1.830000-18100 3102 1082

2.050000+1 1.500000-1 2.690000+1 1.490000-1 2.938000+1 1.620000-18100 3102 1083

3.090000+1 1.700000-1 3.253000+1 1.820000-1 3.434000+1 1.930000-18100 3102 1084

3.628000+1 2.100000-1 3.762000+1 2.220000-1 3.806000+1 2.250000-18100 3102 1085

…

…

1.000000+5 3.500800-2 2.000000+5 3.101000-2 3.000000+5 2.800600-28100 3102 1095

4.000000+5 2.500800-2 5.000000+5 2.251000-2 6.000000+5 2.050600-28100 3102 1096

8.000000+5 1.730200-2 1.000000+6 1.504900-2 1.500000+6 1.053500-28100 3102 1097

2.000000+6 8.500700-3 2.500000+6 7.006600-3 3.000000+6 5.003700-38100 3102 1098

4.000000+6 3.808600-3 5.000000+6 2.506500-3 6.000000+6 2.000500-38100 3102 1099

8.000000+6 1.205300-3 1.000000+7 7.801200-4 1.200000+7 8.276500-48100 3102 1100

1.400000+7 9.003600-4 1.600000+7 7.510600-4 1.800000+7 7.036500-48100 3102 1101

2.000000+7 6.210500-4                                            8100 3102 1102