GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Case Saver

For best results, always start the installation with a clean quad.  Remove the stock or current part from around the sprocket.  Then, remove the shifter and the chain roller.  Place the case saver on the motor.  Snug the bolts for the motor, check the alignment on the welded chain roller mounting tab (because this is a welded part, they are not always in the exact location).  Slot if needed, so you can use your fingers to start the mounting bolt.  Do not pry to align.  Use the washers, as needed, for the gap between the case saver and the chain roller mounting tab.  Check that the shift shaft moves freely; over tightening the chain roller bolt or improper spacing may put a bind on the shift shaft.  Use the nut that is included to double nut if wanted, or in case the factory nut is missing or is damaged.

Note:  We recommend using Loctite Blue Threadlocker for the installation of all mounting hardware.  Please refer to the Factory Honda Service Manual for torque specifications for each bolt size.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Swing Arm Chain Slide

For best results, always start the installation with a clean quad.  The Swing Arm Chain Slide only fits the stock swing arm.  Remove the swing arm to install.  If needed, please refer to the Factory Honda Service Manual for instructions.  Inspect your front counter sprocket for signs of wear; replace if worn.  Also, inspect the swing arm bearings and then lube the swing arm bolt with anti-seize lubricant before reinstalling.  (This process works best if the rear wheels and axle are removed from the swing arm.)

Thou the installation is timely, the part was designed to prevent the chain from getting between the front counter sprocket and the swing arm.  An additional bonus, if the front counter bolt would work its way loose or come off the quad, then your front counter sprocket will stay in position.

Note:  We recommend using Loctite Blue Threadlocker for the installation of all mounting hardware.  Please refer to the Factory Honda Service Manual for torque specifications for each bolt size.  Do not modify this part in any way; it will prevent the part from working as designed and will void the warranty.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Rear Chain Guide for Skid Plate

For best results, always start the installation with a clean quad.  The Rear Chain Guide fits the stock swing arm only.  It works with stock, PRM, and Pro Armor skid plates.

Loosen your chain and skid plate bolts.  Install the chain guide using the hardware that is included.  Re-adjust your chain and tighten your skid plate bolts.

If installing this part on a Honda 400EX/X with a Honda 450R swing arm conversion, some washers are needed behind the Chain Guide for proper clearance of the chain. The chain needs to be centered through the chain guide.

Note:  We recommend using Loctite Blue Threadlocker for the installation of all mounting hardware.  Please refer to the Factory Honda Service Manual for torque specifications for each bolt size.  Do not modify this part in any way; it will prevent the part from working as designed and will void the warranty.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                    Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Rear Chain Guide for Rock Ring or No Skid Plate

For best results, always start the installation with a clean quad.  The Rear Chain Guide fits the stock swing arm only.  Your rotor guard may need to be notched for the mounting block to fit.  Loosen the chain and install all hardware.  Re-adjust your chain and tighten all hardware.

If you are installing this part on a Honda 400EX/X with a Honda 450R swing arm conversion some washers are needed behind the Chain Guide for the proper clearance of the chain. The chain needs to be centered through the chain guide.

Note:  We recommend using Loctite Blue Threadlocker for the installation of all mounting hardware.  Please refer to the Factory Honda Service Manual for torque specifications for each bolt size.  Do not modify this part in any way; it will prevent the part from working as designed and will void the warranty.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Block Off Plate with Cooling Fins

For best results, always start the installation with a clean quad.  This part fits all Japanese quads, from 1985 to current date, with the factory parking brake system.  In the event you are using long travel suspension, the use of an air box lifter kit is a must or you may choose to modify your air box for needed clearance.

Note:  We recommend using anti-seize lubricant for the installation of all mounting hardware.  Also, a good coating of grease on the brake caliper post is recommended, due to the rapid heating and cooling of the brake, moisture may accumulates between the caliper and the block off plate. Please refer to the Factory Service Manual for torque specifications for each bolt size.  Do not modify this part in any way; it will prevent the part from working as designed and will void the warranty.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Tie Rod End Castle Nut Upgrade Kit

For best results, always start the installation with a clean quad.  Remove the tie rod and the ends as a set.  On the bench, chase your stock holes out with a  3/32 drill bit.  On the 400EX you will remove a slight amount of steel.  On the 450R you are just cleaning out the stock hole.  Please make sure the cotter pin fits in each hole before reinstalling on your quad.  The castle nut slot is 3/32 and the tie rod end hole is 3/32  therefore, the alignment of the castle nut slot and the tie rod end hole must be “spot on” for the cotter pin to go in.  (The pin should go in effortlessly, do not force it.) The spindle side is straight forward, but on the stem side, you will need to make sure the tie rod hole faces front-to-back with the stem centered.  This is done to make putting the cotter pin in easier.  On the 450R stem, completely install one side.  The next side, at the steering stem, you will need to use an open ended wrench to tighten the other nut because the ends are so close together.

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com

GLANN INNOVATIONS, LLC

1412 Merle Hay Road    Des Moines, Iowa 50311                                     Office: (515) 528-9056     Cell (515) 979-5241

Installation Instructions

Swing Arm Pivot Bolt

For best results, always start the installation with a clean quad.  Install the Swing Arm Pivot Bolt as normal.  Tighten the castle nut to manufacturers suggested torque, making sure it aligns with the cotter pin hole.  If that hole is not up-and-down then loosen the castle nut, rotate the bolt so that the aligned hole is up-and-down.  Retighten bolt and install cotter pin from top-to-bottom.  The next time you remove this bolt, you can not use excessive force because you will damage the cotter pin holes on the threaded end.  For best results, use the grease zert to lube the bolt after every wash.  (If you do not grease this bolt as described it will seize.)

Thank you for purchasing our parts!  Please contact us if you are in need of future assistance.  Warranty direct.  The purchaser made the decision to use and/or install the above mentioned parts and will assume all liability.  Glann Innovations shall not be held liable for any damages, expenses nor injuries.

Proudly made in the U.S.A.

If you would like, please Facebook us a picture of your quad with our parts on it.  We will add the picture to our Customer Photo Album.  Thank you!

Glann Innovations

Facebook: Glann Innovations

GlannInnovations@hotmail.com