ISC-Silkworm

AMiT, spol. s r.o. does not provide any warranty concerning the contents of this publication and reserves the right to change the documentation without obligation to inform anybody or authority about it.

This document can be copied and redistributed under following conditions:

- The whole text (all pages) must be copied without any changes.

- All redistributed copies must retain the AMiT, spol. s r.o. copyright notice and any other notices contained in the documentation.

- This document must not be distributed for purpose making of profit.

The names of products and companies used herein can be trademarks or registered trademarks of their respective owners.

AMiT is a registered trademark

Copyright (c) 2011, AMiT, spol. s r. o.

Producer: AMiT, spol. s r. o.

Naskové 3/1100, 150 00 Praha

www.amit.cz

Technical support: support@amit.cz

Obsah

History of revisions	5

Related documentation	5

1.	Introduction	6

2.	Audio system	7

2.1.	System commissioning	7

2.2.	Notebook configuration	7

2.3.	Firmware version	8

2.4.	Downloading ICT/A11 and setting IP address	8

2.5.	Downloading MCT/D20 in the driver cabine	8

2.6.	Downloading MCT/D20 at the rear	9

2.7.	Downloading  MC/A	9

2.8.	Downloading PWA/A	9

2.9.	Upgrading audio components firmware	9

2.10.	Verifying firmware version	10

3.	HMI	12

3.1.	Oživení	12

3.2.	Aktualizace	12

4.	Camera system	13

4.1.	Cameras commisioning	13

4.1.1	Camera Identification	13

4.1.2	Firmware Upgrade	15

4.1.3	Loading of configuration template	17

4.1.4	Camera lens setup (positioning and focusing)	21

4.1.5	Deleting camera from ACM database	25

4.2.	Recording unit	26

4.2.1	Check of power supply connector wiring	26

4.2.2	IP address set up	26

4.2.3	Loading application	28

4.2.4	Verifying of loaded application	32

4.2.5	Load the application via web interface	32

4.2.6	Verification of loaded application via web interface	37

5.	LED panels	40

5.1.	System commissioning	40

5.1.1	Address setting	40

5.1.2	Firmware download	41

5.1.3	Test	41

6.	APPENDIX D - Program set	43

6.1.	Camera - AM3114-R/A	43

6.2.	LED panels	43

6.3.	Audio system	44

7.	APPENDIX E – Configuration parameters	47

7.1.	IP addres setting up	47

7.2.	Recording Unit	47

7.3.	Cameras	47

Login data	47

Network settings	48

8.	Appendix F – Axis Camera Management (ACM)	49

Installation	49

First start – password setup	49

9.	Appendix G – IP cameras	51

9.1.1	Operation thru web interface of the camera	51

9.1.2	Description of web interface window	51

9.1.3	Web interface login	52

9.1.4	Live View – live image from camera	53

9.1.5	Creating of Server Report	53

9.2.	Restoring the factory setting	55

9.2.1	Software way of Restoring the factory setting	55

9.2.2	Hardware way of Restoring the factory setting	57

9.3.	Meaning of camera LED indicators	58

10.	Appendix H – Recording unit OS update	59

10.1.1	Create bootable USB flash disk	59

10.1.2	Run recording unit from USB flash disk	62

10.1.3	Verifying version of OS	63

11.	Appendix	64

#### History of revisions

Document name: isc-silkworm_mm_en_103.doc.pdf

Author: Martin Vosáhlo

| Revision | Date | Changes |
| --- | --- | --- |
| 099 | 3. 9. 2013 | New document |
| 100-103 | 4.9.2013 | Working versions |
| 104 | 13.9.2013 | Audio systém commisioning |

#### Related documentation

Help to the development enviroment DetStudio

Application note AP0016 – Zásady používání RS485
file: ap0016_cz_xx.pdf

# Introduction

This manual describes the assembly procedure and commissioning of the information system for tramway Silkworm-Durmazlar.

Information system consists of

HMI panel (Information Control Unit)

LED panels

Audio system (microtelephones, intercoms, ip amplifier)

Cameras

Cameras recording unit

# Audio system

Audio system is consist of following devices:

| Label | Hardware | Quantity | Description |
| --- | --- | --- | --- |
| MCT | RRAS-MCT/D20 | 2 | IP microtelephone at drivers cabine |
| MCT-REAR | RRAS-MCT/D20 |  | IP microtelephone at the rear of tram |
| ICT-x | RRAS-ICT/A11 | 5 | IP intercoms |
| PWA | RRAS-PWA/A | 1 | IP amplifier |
| MC | RRAS-MC/A | 1 | Space microphoneused for balancing the saloon speakers volume |
| GNM | RRAS-GNM/A | 1 | Goosneck microphone |

## System commissioning

Audio system commissioning is divided to 4 separate procedures

Downloading  - downloading unit firmware for the very first time. It is the case of device that is equipped with firmware downloaded in the production. All type of units have the same ip address, so the downloading must be done either in a configuration point-point or with other devices switching off.

IP address setting – this procedure will assign proper ip addresses on the vehicle Ethernet net. IP address setting is necessary only for ICT/A11 devices, other devices have their IP address coded in the firmware.These two steps should be done together on one device, first downloading, then setting IP address.

schema

Verifying firmware version – this procedure will test current version of units firmware

Upgrading – downloading unit firmware in case of new version of firmware

All the steps are done with the help of notebook connected either on Ethernet either to unit itself or to the vehicle Ethernet.

## Notebook configuration

For all operation the notebook Ethernet interface should be set

| IP address | NB_IP_AUDIO |
| --- | --- |
| Net mask | NB_MASK |
| Default gateway | Do not fill |

Values are described in the Appendix XXX.

## Firmware version

Current firmware version are in the table in Appendix XXX.

## Downloading ICT/A11 and setting IP address

- Connect notebook to the Ethernet. Make sure others audio units are switched of.

- Run load_ict.bat batch file from the current Program set (see Appendix XXX).

- Switch off device.

- Press restore button (backside of the device) and switch on the device.

- By pressing button on the front side of device set appropriate IP address of the device according the table below. On the screen there are bold vertical lines. Number of these lines set the offset to IP address.

- When certain time elapses, the screen returns to the operating state. Then restart the device again.

| ICT | Number of lines (offset) | IP address |
| --- | --- | --- |
| ICT-1 | 0 | 192.168.0.184 |
| ICT-2 | 1 | 192.168.0.185 |
| ICT-3 | 2 | 192.168.0.186 |
| ICT-4 | 3 | 192.168.0.187 |
| ICT-5 | 4 | 192.168.0.188 |

Obrazek obrazovky nastavovaci

## Downloading MCT/D20 in the driver cabine

- Connect notebook to the Ethernet. Make sure others audio units are switched of.

- Run load_mct_master.bat batch file from the current Program set (see Appendix XXX).

- Restart the device.

## Downloading MCT/D20 at the rear

- Connect notebook to the Ethernet. Make sure others audio units are switched of.

- Run load_mct_rear.bat batch file from the current Program set (see Appendix XXX).

- Restart the device.

## Downloading  MC/A

- Connect notebook to the Ethernet. Make sure others audio units are switched of.

- Run load_mc.bat batch file from the current Program set (see Appendix XXX).

- Restart the device.

## Downloading PWA/A

- Connect notebook to the Ethernet. Make sure others audio units are switched of.

- Run load_pwa.bat batch file from the current Program set (see Appendix XXX).

- Restart the device.

## Upgrading audio components firmware

This procedure can be done if the downloading (and setting ip address were already done.

Upgrading firmware does not need to switch off other audio devices as all devices have their correct ip address.

Upgrading firmware should be done when new firmware version is released.

- Connect notebook to the vehicle ethernet.

- Run appropriate batch file for certain device according table below from the current Program set (see Appendix XXX).

| Device label | Batch file |
| --- | --- |
| ICT-1 | upgrade_ict1.bat |
| ICT-2 | upgrade_ict2.bat |
| ICT-3 | upgrade_ict3.bat |
| ICT-4 | upgrade_ict4.bat |
| ICT-5 | upgrade_ict5.bat |
| MCT | upgrade_mct_master.bat |
| MCT-REAR | upgrade_mct_rear.bat |
| MC | upgrade_mc.bat |
| PWA | upgrade_pwa.bat |

## Verifying firmware version

This procedure verify the firmware version by reading it from the device.

- Connect notebook to the vehicle ethernet.

- Run appropriate batch file for certain device according table below from the current Program set (see Appendix XXX).

| Device label | Batch file |
| --- | --- |
| ICT-1 | verify_ict1.bat |
| ICT-2 | verify _ict2.bat |
| ICT-3 | verify _ict3.bat |
| ICT-4 | verify _ict4.bat |
| ICT-5 | verify _ict5.bat |
| MCT | verify _mct_master.bat |
| MCT-REAR | verify _mct_rear.bat |
| MC | verify _mc.bat |
| PWA | verify _pwa.bat |

Firmware version can be found in the screen output.

Obrázek výstupu

# HMI

## Oživení

## Aktualizace

# Camera system

AM3114-R/A

PPM2100/2T

## Cameras commisioning

Commissioning of IP cameras consists of following steps:

- Camera identification

- Firmware upgrade

- Loading of configuration template

- Camera lens setup

##### Equipment needed

Service notebook.

axis_acm_200058 - Axis Camera Management (see Appendix D). ACM installation is described in Appendix F.

isc-silkworm_am3114_cfg_200 - configuration templates (see Appendix D).

Tool for dismounting of camera housing.

Tool for loosing of lens thread.

##### Initial state

Before start of camera installation is necessary to set camera system into following state:

- Powering of all components are switched off

- All cameras are disconnected from Ethernet

- Service PC with installed ACM is connected

- The database in ACM does not involve cameras connected before (otherwise they must be deleted.

Setting of service notebook network adapter:

IP address: 			“NB_IP_AXIS”

Subnet mask: 		“NB_MASK”

Default gateway: 		do not fill

### Camera Identification

Plug the Ethernet cable into the appropriate connector of particular camera and wait for about 30 s (time for camera start up).

Launch the ACM on service PC and click on Search icon on Toolbar.

ACM – the Search icon

In the next dialog enter the value of „IP range“ for searching (Chyba! Nenalezen zdroj odkazů., Chyba! Nenalezen zdroj odkazů.) and confirm by OK button.

ACM – Network search dialog

If the search is unsuccessful and no camera is found, repeat this procedure.

Camera which has been found is shown in ACM Main window.

ACM – New camera is found

### Firmware Upgrade

Select the camera by left mouse button click and launch the upgrading dialog by Upgrade button from Toolbar.

Upgrade button / icon

In the next dialog box click on <Select> and select .bin file with new firmware version.

Selection of file with firmware

By checking the „Upgrade device in:“ radio button  we can affect the upgrade process, when a bulk upgrading of more cameras is made.

Parallel – cameras will be upgraded all at once

Sequence – cameras will be upgraded sequentially

Progress of upgrade process

Wait for upgrade completion.

Upgrade recapitulation

Finally, a recapitulation window is shown, which presents a list of upgraded cameras and results of upgrades.

### Loading of configuration template

Select the camera in ACM Main window by left mouse button click. Click on icon Apply Template on the Toolbar and the menu for selection of configuration template is displayed.

ACM – Looking for template

Through item Browse open a next window with list of configuration templates.

ACM – Selection of configuration template

Choose the configuration template, which is determined for connected camera.

Templates

After opening the configuration template a dialog box appears, that contains set of camera parameters which can be changed. Confirm this dialog by OK button and changes in setting the camera are applied.

Modified parameters

After applying of configuration template a recapitulation window is shown which contains result of loading and overview of all recently set parameters.

Recapitulation of changes performed in parameters

After pressing the Close button is configuration of camera parameters completed.

### Camera lens setup (positioning and focusing)

The whole process of setting the camera lens is realized in following steps:

- Viewing the image from camera on service notebook.

- Taking off the camera cover.

- Camera lens position setup

- Focusing the camera lens.

- Deleting camera from ACM database.

For mechanical adjusting of camera is used special tool composed of two parts: holder and the turning part.

Tool for adjusting lens

The turning part is used for:

- Focusing the camera lens.

- Position setting of head with lens.

##### Zobrazení obrazu

Setting of service notebook network adapter:

IP address: 			“NB_IP_CAM”

Subnet mask: 		“NB_MASK”

Default gateway: 		do not fill

Launch the internet browser on service notebook and enter into address field the IP address of camera, which will be focused / positioned.

Entering the camera IP address

Internet Explorer needs an ActiveX control for its operation. If not installed yet, you will be prompted to install it.

Installation of an ActiveX control

After installation is opened a login dialog, where login data for web access need to be entered:

User name: 	“CAM_Login”

Password: 	“CAM_Password”

Image from camera is displayed after click on Live View item, located in heading of web interface.

Launching of Live Vie

##### Taking off the camera cover

To remove the camera cover, two bolts which hold the cover must be released.

The bolts which hold the camera cover

Then, use a special plastic tool or flat screwdriver for lifting up and releasing the camera cover. If you had some resistance, you will need to use appropriate power.

Taking off the camera cover.

After removing the cover you can begin with lens position adjustment.

Legend to camera body

##### Camera lens position setup

Position of camera lens affects the image, which is captured by camera. Positioning is realized by turning the head with lens while the captured image is viewed over Live View on computer screen. Range of positioning is mechanically limited.

Camera lens positioning

When adjusting the camera lens in external housing is important to take into account the peephole through cover front side.

After adjusting the required lens position you can focus the camera image.

##### Focusin the camera lens

Camera is delivered with lens set by manufacturer. Therefore it is necessary to check the image quality, the lens must be focused as best as possible.

Focusing the camera lens

For focusing is used the same tool mentioned above. Turn the lens clockwise or counter clockwise while image sharpness is checked through Live View.

Pay a maximum attention to cleanliness of lens when turning it!

As soon as the focusing is completed, place the upper cover back on the camera..

### Deleting camera from ACM database

After completion of procedures of camera configuration and lens adjusting is necessary to delete in ACM Main window records about cameras, with which it was worked.

The reason is, that there are application problems when cameras with the same IP address are repeatedly detected.

Records are deleted by following way:

- Disconnect the service computer from Ethernet

- Click on All Devices item in the left side of window, section Groups

- Click in the window central part, (where is the list of cameras) on camera and mark the all cameras (e.g. by Ctrl+A shortcut key)

- From Main Menu select the Edit / Delete From Database option

- Confirm the dialog „This will delete the selected device from the database. Continue?“ by pressing Yes button.

After confirming the previous dialog, in the left window side, section Groups will be displayed: All Devices (0)

## Recording unit

Commissioning of recording unit consists of following steps:

- Check of power supply connector wiring

- Loading application

- Verifying version of loaded application

###### Equipment needed

Notebook with FTP client (TotalComander is recommended).

Application ().

### Check of power supply connector wiring

Checking of proper wiring of recording unit powering is necessary before the first unit switch on.

For switching unit off must be essentially used the terminal labelled SB. Terminal with label +U must be permanently connect to the vehicle battery.

Recording unit power supply wiring

Only this connection ensures the faultless unit operation.

###### SB function

| SB | Device state |
| --- | --- |
| +U | Device is ON |
| not connected | Device is OFF |

When disconnecting SB, then start sequence for turning off the system. During this time auxiliary CPU sends to main CPU turning off signal.

Immediately after successful main CPU turn-off, the whole Recording Unit is disabled. If the main CPU is not switched off due to failure, Recording Unit is after 1 minute switched off automatically.

Disconnecting of supplying conductors is done only after previous Recording Unit switching-off through SB signal. If not, you may lose data.

### IP address set up

Turn the recording unit power supply on and wait for about 1 minute.

Connect the service notebook to vehicle Ethernet network and start the AmitDeviceDetection.exe tool.

AmitDeviceDetection start up

Wait, while the Ethernet network is scanned.

Searching the device

Click by right mouse button on the recording unit being found and select Change IP settings from context menu.

Change of IP address

Enter the parameters you want to set on recording unit:

IP Address: 			„RU_IP_A“

Subnetwork mask: 		„RU_MASK“

Gateway: 			do not fill

Confirm by OK and wait for new search of recording unit with new parameters.

IP address setup

### Loading application

To load a new version of an application into recording unit is necessary to perform the following steps:

- Connect to FTP server

- Delete old application

- Copying of new application files

- Restart recording unit

In following procedure is used TotalCommander 7.5a for connection to FTP, but files can be loaded through any FTP client.

##### Connect to FTP server

Launch TotalCommander and select from Main menu

Net --> FTP Connect

TC – Main menu

In dialog Connect to FTP server click on the button

New connection..

TC – Connect to the FTP server

Enter the parameters to connect to recording unit:

Session:		RU

Host name (:Port):	192.168.0.xxx

User name:		service

Password:		remote

TC – Parameters Monitor_A

Press Connect button.

TC – Connect to Monitor_A

##### Delete old application

Identify, in which tab are displayed files from connected monitor (from heading bar - see figure).

TC – Identification of FTP contents

Go to the /app directory and delete all files.

Application files

##### Copying of new application

Copy the new version of application from actual program set.

After completion of copying process press the Disconnect button.

##### Restart recording unit

Turn off and on the recording unit.

After restart it will be use new version of application.

### Verifying of loaded application

IP address:			192.168.0.xx

Subnet mask:		255.255.255.0

Default gateway:		not filled

Run internet browser (i.e. Internet Explorer).

Into the line for address setting enter the command:

192.168.52.205 Version of application, which is loaded in Recording unit, you can get from response to http request info.

Setting of service notebook network adapter:8888/info

Confirm the command by Enter key.

Browser shows xml file as response on send request.

The version number is between these two tags

<version>........</version>

Identification of version

### Load the application via web interface

To load a new version of an application into recording unit it is necessary to perform the following steps:

- Connect to WEB server

- Copying of new application files

- Restart recording unit

In following procedure is used Firefox 23.0.1 for connection to WEB, but files can be loaded through any WEB browser.

##### Connect to WEB server

Setting of service notebook network adapter:

IP Address: 			„NB_IP_PPM“

Subnetwork mask: 		„NB_MASK“

Gateway: 			do not fill

Run internet browser.

Into the line for address write address of record unit:

https://<ru_ip>, where <ru_ip> is IP address of recording unit (e.g. https://192.168.0.120)

Entering the address into the address line

Confirm the address by Enter key and then you can see the web interface of unit (main menu), see figure. Here click to service link.

Service link

To the next dialog window you will need entered following login and password.

User name:	“PPM_LOGIN”

Pasword:		“PPM_PASS”

Click to OK button.

Authentication

In the next window simply click to upgrade link.

Upgrade link

And then click to Procházet (Browser) button.

Procházet (Browse) button

In the next dialog window you must choose the file which you want upload to record unit. And then click to Otevřít (Open) button.

Otevřít (Open) button

In the next window click to Upload button.

Upload button

Now you need reboot the record unit. You can do it by click to reboot link.

Reboot link

And then click to Reboot! button.

Reboot button

Now you must wait few minutes. During the waiting you can try to connect to record unit by clicking to connect link. If the connection is unsuccessful, then record unit still booting.

Connect link

After reboot and success connect you will see main menu of recording unit.

### Verification of loaded application via web interface

Version of application, which is loaded in Recording unit, you can get from web interface.

- Connect to WEB server

In following procedure is used Firefox 23.0.1 for connection to WEB, but it can be used any web browser.

##### Connect to WEB server

Setting of service notebook network adapter:

IP Address: 			„NB_IP_PPM“

Subnetwork mask: 		„NB_MASK“

Gateway: 			do not fill

Run internet browser.

Into the line for address enterded address of record unit:

https://<ru_ip> (e.g. https://192.168.0.120)

Typing the address into the address line

Confirm the address by Enter key and then you can see the main menu of recording unit. Here click to application link.

Application link

In the following window you can see the version of loaded application.

The number of version is highlighted by red rectangle.

Highlighted number of version

# LED panels

ALP2200/AB

ALP2300/A

ALPC0510/A1

Audio system is consist of following devices:

| Label | Hardware | Quantity | Description |
| --- | --- | --- | --- |
| MCT | RRAS-MCT/D20 | 2 | IP microtelephone at drivers cabine |
| MCT-REAR | RRAS-MCT/D20 |  | IP microtelephone at the rear of tram |
| ICT-x | RRAS-ICT/A11 | 5 | IP intercoms |
| PWA | RRAS-PWA/A | 1 | IP amplifier |
| MC | RRAS-MC/A | 1 | Space microphoneused for balancing the saloon speakers volume |
| GNM | RRAS-GNM/A | 1 | Goosneck microphone |

## System commissioning

Commissioning consist from following steps:

- Addresses setting (RS485)

- Downloading firmware

- Test

### Address setting

Power off all panels..

Set the address by means of configuration connector X2 according following table.

| Address | PIN |
| --- | --- |
|  | 2 | 3 | 4 | 5 |
| 64 | No | No | No | No |
| 65 | Yes | No | No | No |
| 66 | No | Yes | No | No |
| 67 | Yes | Yes | No | No |
| 68 | No | No | Yes | No |
| 69 | Yes | No | Yes | No |
| 70 | No | Yes | Yes | No |
| 71 | Yes | Yes | Yes | No |

Yes – connection to pin 1

No – not connected to pin 1

| Panel | Location | Panel label | Address |
| --- | --- | --- | --- |
| ALP2200 | Front panel, front | ALP2200_F | 64 |
| ALP2200 | Front panel, rear | ALP2200_R | 65 |
| ALP2300 | Side panel, front | ALP2300_F | 66 |
| ALP2300 | Side panel, rear | ALP2300_R | 67 |
| ALP3C | Internal, 1 | ALP3C_1 | 68 |
| ALP3C | Internal, 2 | ALP3C_2 | 69 |
| ALP3C | Internal, 3 | ALP3C_3 | 70 |
| ALP3C | Internal, 4 | ALP3C_4 | 71 |

### Firmware download

Connect notebook to the RS485 by means of RS485 converted (mostly USB/RS485 converter).

Power on panels.

From the command line run the batch files

load_yyyyyy.bat X

where parameter X is a numer of COM port.

| Panel | Location | Panel label | Batch file |
| --- | --- | --- | --- |
| ALP2200 | Front panel, front | ALP2200_F | load_alp2200_f.bat |
| ALP2200 | Front panel, rear | ALP2200_R | load_alp2200_r.bat |
| ALP2300 | Side panel, front | ALP2300_F | load_alp2300_f.bat |
| ALP2300 | Side panel, rear | ALP2300_R | load_alp2300_r.bat |
| ALP3C | Internal, 1 | ALP3C_1 | load_alp3c_1.bat |
| ALP3C | Internal, 2 | ALP3C_2 | load_alp3c_2.bat |
| ALP3C | Internal, 3 | ALP3C_3 | load_alp3c_3.bat |
| ALP3C | Internal, 4 | ALP3C_4 | load_alp3c_4.bat |

### Test

Připojte notebook do sítě RS485 (blokové schéma, konektor).

Zapněte napájení všech informačních panelů.

Z příkazového řádku spusťte dávku:

test.bat X

Parametr X má význam čísla COM portu, na který je namapován připojený převodník RS485toUSB.

Po odeslání dávky se xxx vteřin na všech panelech rozsvítí kontrolní text s jejich označením.

# APPENDIX D - Program set

Actual program set: 130903_ISC-SILKWORM

Download link: http://imp.amit.cz/www/isc-silkworm/index.html

## Camera - AM3114-R/A

| Directory | File | Description |
| --- | --- | --- |
| isc-silkworm_am3114_cfg_200 | ks-silkworm_CAM1-1_200.cmt | Config. template CAM1-1 |
|  | ks-silkworm_CAM1-2_200.cmt | Config. template CAM1-2 |
|  | ks-silkworm_CAM2_200.cmt | Config. template CAM2 |
|  | ks-silkworm_CAM4_200.cmt | Config. template CAM4 |
|  | ks-silkworm_CAM5-1_200.cmt | Config. template CAM5-1 |
|  | ks-silkworm_CAM5-R_200.cmt | Config. template CAM5-R |
|  | ks-silkworm_CAM-L_200.cmt | Config. template CAM-L |
|  | ks-silkworm_CAM-R_200.cmt | Config. template CAM-R |
|  | M3114-R_5_40_9_2.bin | Firmware |
| axis_acm_200058 | axis_acm_2.00.058.exe - | Installation file |

## LED panels

| Directory | File | Description |
| --- | --- | --- |
| isc-silkworm_alp_fw_121 | load_alp3c_1.bat | Batch file for downloading the firmware |
|  | load_alp3c_2.bat | Batch file for downloading the firmware |
|  | load_alp3c_3.bat | Batch file for downloading the firmware |
|  | load_alp3c_4.bat | Batch file for downloading the firmware |
|  | load_alp2200_f.bat | Batch file for downloading the firmware |
|  | load_alp2200_r.bat | Batch file for downloading the firmware |
|  | load_alp2300_f.bat | Batch file for downloading the firmware |
|  | load_alp2300_r.bat | Batch file for downloading the firmware |
|  | alp3c_a_121.elf | Firmware |
|  | alp22_a_121.elf | Firmware |
|  | alp23_a_121.elf | Firmware |
|  | Fido.exe | Tool for downloading |

## Audio system

| Directory | File | Description |
| --- | --- | --- |
| isc-silkworm_rras_fw_137 | load_ict.bat | Batch file for downloading the firmware to RRAS-ICT/A11 |
|  | load_mc.bat | Batch file for downloading the firmware to RRAS-MC/A |
|  | load_mctd_master.bat | Batch file for downloading the firmware to RRAS-MCTD/D20 located in drivers cabine |
|  | load_mctd_rear.bat | Batch file for downloading the firmware to RRAS-MCT/D20 located at the rear |
|  | load_pwa.bat | Batch file for downloading the firmware to RRAS-PWA/A |
|  | upgrade_ict1[-5].bat | Batch file for upgrading firmware to RRAS-ICT/A11 at location 1 to 5 |
|  | upgrade_mc.bat | Batch file for upgrading the firmware to RRAS-MC/A |
|  | upgrade_mctd_master.bat | Batch file for upgrading the firmware to RRAS-MCTD/D20 located in drivers cabine |
|  | upgrade_mctd_rear.bat | Batch file for upgrading the firmware to RRAS-MCTD/D20 located at the rear |
|  | upgrade_pwa.bat | Batch file for upgrading the firmware to RRAS-PWA/A |
|  | ict-a11_2_a_137.elf | Firmware for RRAS-ICT/A11 |
|  | mc-a1_1_a_137.elf | Firmware for RRAS-MC/A |
|  | mct-d20_2_a_137.bin | Firmware for RRAS-MCT/D20 located in the drivers cabine |
|  | mct-d20_3_a_137.bin | Firmware for RRAS-MCT/D20 located at the rear |
|  | pwa-a_1_a_137.bin | Firmware for RRAS-PWA/A |
|  | TOOLS\Silkworm_Configurator_200.exe | Tool for downloading and updating firmware |

# APPENDIX E – Configuration parameters

In following tables are presented parameters, which serves for working with camera system or which are used for configuration and service operations.

For several parameters is used a Symbolic name system. The symbolic name is in previous chapters represented as „Symbolic name“. Instead of this name in described operation is necessary to enter a Value, which is presented in tables below.

## IP addres setting up

| Symbolic name | Value |
| --- | --- |
| IP_Range | 192.168.0.* |
| NB_IP_AIPM | 192.168.0.112 |
| NB_IP_PPM | 192.168.0.112 |
| NB_IP_AXIS | 192.168.0.112 |
| NB_IP_CAM | 192.168.0.112 |
| NB_IP_ERT | 192.168.0.112 |
| NB_MASK | 255.255.0.0 |
| NB_IP_AUDIO | 192.168.0.112 |

## Recording Unit

## Cameras

| Camera | IP Address | Location | Configuration template |
| --- | --- | --- | --- |
| CAM1-1 | 192.168.0.120 | Module 1 | ks-silkworm_CAM1-1_xxx.cmt |
| CAM1-2 | 192.168.0.121 | Module 1 | ks-silkworm_CAM1-2_xxx.cmt |
| CAM2 | 192.168.0.122 | Module 2 | ks-silkworm_CAM2_xxx.cmt |
| CAM4 | 192.168.0.123 | Module 4 | ks-silkworm_CAM4_xxx.cmt |
| CAM5-L | 192.168.0.124 | Module 5 | ks-silkworm_CAM5-1_xxx.cmt |
| CAM5-R | 192.168.0.125 | Module 5 –rear | ks-silkworm_CAM5-R_xxx.cmt |
| CAM-L | 192.168.0.126 | Outside left | ks-silkworm_CAM-L_xxx.cmt |
| CAMR | 192.168.0.127 | Outside right | ks-silkworm_CAM-R_xxx.cmt |

#### Login data

| Symbolic name | Value |
| --- | --- |
| CAM_Login | root |
| CAM_Password | pass |

#### Network settings

| CAM_GW | 192.168.0.254 |
| --- | --- |
| CAM_MASK | 255.255.255.0 |

# Appendix F – Axis Camera Management (ACM)

For detection of cameras and configuration of their parameters is used an effective installation and management tool for IP cameras - Axis Camera Management version 2.00 (in this document referred as ACM).

Axis Camera Management - Main window

##### Link to download

ACM can be downloaded from Axis company website. Direct link to download (verified to date 2012.08.23):

http://www.axis.com/products/cam_mgmt_software/index.htm

Download is conditioned by free of charge registration.

#### Installation

Does not require any special settings All options can be default.

#### First start – password setup

At the first launch is automatically activated the Set Master Credentials dialog box.

Master Credentials setting

User name and Password will be used afterwards for accessing cameras, therefore they need to be set in accordance with Chyba! Nenalezen zdroj odkazů., Login data:

User name: 		„CAM_Login“

Password: 		„CAM_Password“

Access: 		checked

# Appendix G – IP cameras

### Operation thru web interface of the camera

Besides automatic configuration via ACM can be camera parameters changed also through web configuration interface, which each Axis camera contains.

###### Warning:

Any intervention to camera configuration (except for actions described below) are not recommended. They can affect negatively the image quality and camera performance.

The procedures described below assume that we are working with the camera, which has its IP address already assigned.

### Description of web interface window

The web interface window can be divided into three parts:

Heading – toggling of Parameterization section (Live View / Setup) and viewing of context help

- Live View – live image from camera

- Setup – parameters setting

Left side menu – navigation in Parameterization section parameters

Parameterization section – performing of service operations and changing of settings

Description of web interface window

### Web interface login

All operations described in following chapters require previous separate web interface login.

Launch the internet browser (Internet Explorer is recommended) and enter into address field an IP address of camera, web interface of which you want to view.

Entering of camera IP address

Internet Explorer needs an ActiveX control for its operation. If not installed yet, you will be prompted to install it.

ActiveX control enabling.

After installation is opened a login dialog, where login data for web access need to be entered:

User name: 	„CAM_Login“

Password: 	„CAM_Password“

Web interface login dialog

After login, an entry site of web interface is displayed. Click on Setup item in web interface Heading.

Displaying of parameters setting

### Live View – live image from camera

Image from camera is displayed after click on Live View item, located in web interface Heading.

Displaying of live image from camera

### Creating of Server Report

In starting screen select the section System Options in Left menu.

System Options section

Then, proceed into subsections:

Support ( Logs & Reports ( Information.

Navigation in System Options section

Generate the Server Report by click on appropriate button. Then it will be available in right - Parameterization - window part.

Generating of Server Report

Finally, new dialog window appears, where is shown the Server Report, which can be copied into text file and sent for analysis.

View on Server Report

## Restoring the factory setting

You can restore the original factory setting. It can be done by two ways:

- By software way – restores the factory setting of parameters including/ with exception of (optionally) Ethernet interface.

- By hardware way – factory setting of all parameters.

After resetting is the camera considered as quite new and next steps can be performed in accordance with Chyba! Nenalezen zdroj odkazů. Chyba! Nenalezen zdroj odkazů..

### Software way of Restoring the factory setting

Login to camera web interface (see Appendix G – IP cameras, Web interface login).

In starting screen select the section System Options and Maintenance sub-section in Left menu.

Factory settings through software - menu

Screen with several buttons is displayed. Their meaning is evident from labels.

Software way of Restoring the factory setting

Restore – IP address is retained, all another parameters are reseted.

Default – all parameters including IP address are restored.

After click on one of these buttons and confirming in dialog box the camera „freezes“ for several tens of seconds (camera restart is part of all operations).

### Hardware way of Restoring the factory setting

When happens that even by using the ACM the camera cannot be found in network and you are 100 % sure that camera is properly connected into network, then the hardware reset into factory setting is recommended.

Resetting of all parameters including IP address:

- Disconnect the camera network cable

- Dismount the camera cover

To remove the camera cover, two bolts which holds the cover must be released.

The bolts which holds the camera cover

Then, use a special plastic tool or flat screwdriver for lifting up and releasing the camera cover. An appropriate power needs to be applied due to some resistance.

Taking off the camera cover.

Legend to camera body

- Press and hold the Control button, attach the network cable.

- Hold the Control button and wait until LED Status indicator starts light yellow (it can take up to 15 seconds).

- Release the Control button. When the LED Status indicator starts light green (it can take up to 1 minute), process is completed an camera is reseted.

- Perform the camera configuration according to Chyba! Nenalezen zdroj odkazů. Chyba! Nenalezen zdroj odkazů..

## Meaning of camera LED indicators

| LED | Colour | Description |
| --- | --- | --- |
| NET | Green | Connected to 100 Mbit/s network. Blinking indicates the network activity. |
|  | Orange | Connected to 10 Mbit/s network. Blinking indicates the network activity. |
|  | Does not light | Not connected to network. |
| STAT | Green | Camera runs and is OK. |
|  | Orange | Camera start / reset to factory setting is under way. |
|  | Red | Blinks slowly after unsuccessful firmware upgrade. |
| PWM | Green | Power supply is attached. |
|  | Orange | Blinks green/orange when firmware upgrade is under way. |
|  | Does not light | Camera is not powered. |

# Appendix H – Recording unit OS update

Appendix describes how to update operating system of recording unit. Update is made via USB flash disc. OS update consists of following steps:

Create bootalbe USB flash disk

Run recording unit from USB flash disk

##### Equipment needed

USB flash disc with minimal capacity 4 GB.

USB flash disc image (an actual version see Appendix D).

Service notebook.

### Create bootable USB flash disk

Plug in clear the USB flash disc to the service notebook.

Open Start menu and

- click right mouse button on „My Computer“ and from context menu chose  „Manage->Disc Management“

- in Disc Management identify connected USB flash disc

Disc management

Delete all partitions on USB flash disc:

- click right mouse button on USB flash disc partition

- chose Delete partition from context menu”

Delete partition

Confirm partition delete by click Yes.

Disc management - warning

Repeat for all USB flash disc partitions.

USB flash disc without partitions

Open a command prompt as Administrator. Navigate to directory with USB flash disc image and img2usb.exe tool.

Directory selection

Run img2usb tool:

img2usb.exe <usb flash disc file>

Run img2usb.exe tool

Enter the number of the connected USB flash disc to write image.

Disc selection

Check that you choose the right disc and confirm your selection.

Disc confirmation

Do not make any write operation to created USB flash disc and wait until operation is finished.

Image writing in progress

The USB flash disc is ready to use.

Img2usb.exe – successfully written

Safely remove the USB flash disc from the service notebook.

### Run recording unit from USB flash disk

Switch off the recording unit.

Plug in the USB flash disk to USB connector on recording unit.

Switch on the recording unit, this is indicated with short low beep.

Wait a few seconds until the unit boot up.

When update procedures starts, you will hear periodic beep with low/high tone.

During uploading of operating system, you will hear low tone with 4 s gap.

When update procedure ends correctly, you will hear loud melody which ends with high tone. If not, you will hear melody which ends with low tone.

After completion of all operations (can still run the disk check) follow a final melody.

After final melody switch off the recording unit.

Disconnect the USB flash disk.

Switch on the recording unit.

### Verifying version of OS

Version of OS which is loaded in recording unit you can get from the web interface.

###### Procedure

Setting of service notebook network adapter:

IP Address: 			„NB_IP_PPM“

Subnetwork mask: 		„NB_MASK“

Gateway: 			do not fill

Launch the Internet browser (e.g. Internet Explorer).

Enter the https://<ru_ip> address into the address field, where <ru_ip> is IP address of recording unit (e.g. https://192.168.20.120 for recording unit with IP address 192.168.20.120).

Confirm the address by Enter key.

OS version

# Appendix

# Text boxes

Version 1.04

Assembly manual

Passenger information system