KS-630MiL

AMiT, spol. s r.o. does not provide any warranty concerning the contents of this publication and reserves the right to change the documentation without obligation to inform anybody or authority about it.

This document can be copied and redistributed under following conditions:

- The whole text (all pages) must be copied without any changes.

- All redistributed copies must retain the AMiT, spol. s r.o. copyright notice and any other notices contained in the documentation.

- This document must not be distributed for purpose making of profit.

The names of products and companies used herein can be trademarks or registered trademarks of their respective owners.

AMiT is a registered trademark

Copyright (c) 2011, AMiT, spol. s r. o.

Producer: AMiT, spol. s r. o.

Naskové 3/1100, 150 00 Praha

www.amit.cz

Technical support: support@amit.cz

Contents

History of revisions	5

Related documentation	5

1.	Definition of used terms	6

2.	Introduction	7

3.	Technical parameters	8

3.1.	System description	8

3.2.	System functions	8

3.3.	System technical parameters	9

3.4.	Software	9

3.5.	IP monitor states of viewing	10

4.	Putting system into operation	11

4.1.	IP monitors commissioning	11

4.1.1	IP address setting up	11

4.1.2	Loading the actual version of the application	16

Connecting to a FTP server of the IP monitor	16

Deleting previous application files	18

Copying of new application files	19

Camera system restart	19

Verifying of loaded application	19

4.2.	AM3114A cameras commissioning	20

4.2.1	Camera identification	21

Connect camera to Ethernet	21

Finding of connected camera through ACM	21

4.2.2	Firmware upgrade	22

4.2.3	Loading of configuration template	24

4.2.4	Camera lens setup (positioning and focusing)	28

Viewing the image from camera on service notebook	29

Taking off the camera cover	30

Camera lens position setup	31

Focusing the camera lens	32

Deleting camera from ACM database	32

4.3.	MD8562/B cameras commissioning	33

4.3.1	IP address setting up	33

4.3.2	Parameters setting up	42

4.3.3	Camera lens setup	42

4.4.	Recording unit commissioning	44

4.4.1	Check of power supply connector wiring	45

4.4.2	IP address setting up	45

4.4.3	Loading the actual version of an application	47

Connecting to a FTP server of the recording unit	48

Deleting previous application files	50

Copying of new application files	51

Recording unit restart	51

Verifying of loaded application	51

4.5.	ERT03/A2 commissioning	52

4.5.1	Update from ERT/A1 to ERT/A2	52

4.5.2	Parameters setting up	52

4.5.3	Application update	52

5.	APPENDIX A – Location of components	54

6.	APPENDIX B – Scenes	55

7.	APPENDIX C – Block diagram	57

8.	APPENDIX D – Program set	58

IP monitor - AIPM1013/A	58

Camera - AM3114-R/A	58

Camera - MD8562/B	59

Router - ERT03/A2	59

Acasys Studio Vehicle Profile	59

Recording unit - PPM2110/2T	60

9.	APPENDIX E – Configuration parameters	61

9.1.	IP address setting up	61

9.2.	Cameras	61

Login data	62

Network settings	62

9.3.	IP monitor	62

9.4.	Recording unit	62

10.	Appendix F – Axis Camera Management (ACM)	63

Installation	63

First start – password setup	63

11.	Appendix G – IP cameras	65

Operation thru web interface of the camera	65

Description of web interface window	65

Web interface login	66

Live View – live image from camera	67

Creating of Server Report	67

11.1.	Restoring the factory setting	69

Software way of Restoring the factory setting	69

Hardware way of Restoring the factory setting	71

11.2.	Meaning of camera LED indicators	72

12.	Appendix H - Recording unit OS update	73

12.1.	Create bootalbe USB flash disk	73

12.2.	Run recording unit from USB flash disk	76

12.3.	Verifying version of OS	77

#### History of revisions

Document name: ks-630mil_mm_en_102.pdf

Author: Václav Krčmář

| Revision | Date | Changes |
| --- | --- | --- |
| 100 | 22. 05. 2012 | New document |
| 101 | 31. 07. 2012 |  |
| 102 | 01. 08. 2013 |  |

#### Related documentation

Programmer’s manual
file: 630mil_ms_en_xxx.pdf

Operation manual
file: aipm1013a_g_en_xxx.pdf

Operation manual
file: ppm21xx_g_en_xxx.pdf

Programmer’s manual
file: ppm21xx_ms_en_xxx.pdf

User manual
file: acasysstudio_ms_en_xxx.pdf

Operation manual 
file: kkr-m31_g_en_xxx.pdf

Programmer’s manual
file: ert03-a2_ms_en_100.pdf

User Manual Vivotek MD8562 
file: download from http://www.vivotek.com

User Manual Axis M3114-R 
file: download from http://www.axis.com

# Definition of used terms

###### Recording unit

Performs recording of image from cameras on hard disk.

###### IP monitor

Displays the live image from one or more cameras (maximum four). When more than one camera is displayed, quadruple (4Q) mode is used, where monitor screen is splitted into 4 equal rectangulars, into which are directed video streams from cameras.

###### Camera

Performs the image capture and sends the digitized data in MJPEG (Motion JPEG) video stream form via Ethernet.

###### Camera housing

Protection of outdoor IP cameras against climate effects.

###### PoE switch

Switch with possible powering via communication cable (Power Over Ethernet).

###### Scene

Determines the way of viewing information on IP monitor.

Can contain the following items:

- empty screen

- camera number to be displayed on IP monitor

- list of up to 4 cameras, that can be displayed on IP monitor in quadruple mode (4Q) – where the screen is splitted into 4 equal fields; in every field is displayed image from one or none camera

###### Axis Camera Management
(ACM)

Configuration tool for searching camera within network and setting the viewing parameters; for this purpose is used a Configuration template.

###### Configuration template

Configuration file, used for setting of camera parameters through ACM.

# Introduction

This document describes putting into operation and setting the 630MiL (KS-630MiL) engine camera system from software point of view.

Document does not care about mechanical assembly, which is solved in Operation manuals of individual components (see Related documentation).

# Technical parameters

## System description

System functionality is determined by software used in router, IP monitors and recording unit.

Layout of components in vehicle you can find in APPENDIX A – Location of components

## System functions

System function is described in ks-630mil_ms_en_xxx.pdf document.

## System technical parameters

##### IP monitors

| Quantity | 2 pcs. |
| --- | --- |
| Monitor type | AIPM1013/A |
| Address configuration | ADD |
| Viewed data format. | MJPEG |
| Image resolution | 640 x 480 |
| Viewing frame rate | 20 fps |
| Image delay | Max 200 ms |
| Viewing type | Max 4 pictures per screen |

##### Cameras

| Quantity | 14 pcs. |
| --- | --- |
| Camera type | AM3114-R/A |
| Camera housing type | Indoor cameras without housing |

| Quantity | 4 pcs. |
| --- | --- |
| Camera type | MD8562/B |
| Camera housing type | Outdoor cameras without housing |

##### Recording unit

| Quantity | 2 pc. |
| --- | --- |
| Unit type | PPM2110/2T |
| Format of saved video | MJPEG |
| Recording rate | 5 fps |
| Recording resolution | 640 x 480 pixels |
| HDD capacity | 2 TB (plug-in module) |
| Maximum disk utilization | 95 % of overall capacity |
| Timeout at camera disconnection | 5 s |
| SOS state duration | 300 s |
| Service access | FTP |

##### System components

| PPM2110/2T | 2 x | Recording unit with software |
| --- | --- | --- |
| AIPM1013/A | 2 x | IP monitor with software |
| AM3114-R/A | 14 x | Indoor camera |
| MD8562/B | 4 x | Outdoor camera |
| KKR-MD85/C | 2 x | Outer Camera Cover |
| KKR-MD85/D | 2 x | Outer Camera Cover |
| ERT03/A2 | 1 x | Ethernet TCN router for rolling stock |

## Software

Software is published as software package, released at a certain date. Available to download from web:

http://imp.amit.cz/www/kamerove_systemy/pesa/630mil/index.html

Actual software set involves all files needed for whole camera system installation.

Content of actual program set is available at APPENDIX D – Program set

## IP monitor states of viewing

In following table are briefly described states of viewing, which can occur on IP monitor.

| Situation | Description of viewing |
| --- | --- |
| Application is not loaded | Black screen without camera number. |
| Wrongly loaded application | Black screen without camera number. |
| Different version of applications in IP monitors | Black screen without camera number. |
| Video stream blackout | Symbol see Fig. 1 - Video stream blackout symbol |
| No scene is selected | Black screen without camera number. |
| Single camera scene | Camera number in the left bottom corner. |
| Multi camera scene | Mosaic composed from four camera images. Besides the image itself each mosaic part contains also the camera number. |

Video stream blackout symbol

# Putting system into operation

When putting system into operation it is supposed, that all system components are properly mounted, capable of operating and power supply is correctly attached to all units. The ethernet infrastructure must be properly installed and all powering and communication cables must be attached to units. For proper operation of camera system must be used only components mentioned below.

Putting system into operation, consist of following steps:

- IP monitors commissioning

- AM3114A cameras commissioning

- MD8562/B cameras commissioning

- Recording unit commissioning

- ERT03/A2 commissioning

## IP monitors commissioning

IP monitors commissioning consists of following steps:

- IP address setting up

- Loading the actual version of an application

##### Equipment needed

Service notebook with installed FTP client file manager (Total Commander - (TC hereinafter) - is recommended).

ks-630mil_aipm1013a_app - application files (see Appendix D).

ks-630mil_aipm1013a_cfg - configuration files (see Appendix D).

Setting of service notebook network adapter:

IP address: 			“NB_IP_AIPM”

Subnet mask: 		“NB_MASK”

Default gateway: 		do not fill

### IP address setting up

Connect service notebook to vehicle ethernet and turn-off firewall.

Run ALBDConfig.exe and wait until ethernet scan finish.

Searching for AMiT devices

ALBDConfig will find connected IP monitors.

AIPM has been found

Click right mouse button on the first IP monitor and select Assign a profile ... .

Start profile change dialog

New window will show.

Set AIPM to Identification mode

Click on the button Continue and wait about 45 seconds. On the selected IP monitor you will see „AMiT display device VISUAL identification mode“ graphic.

Profile selection

Select IP monitor profile and click on Continue button.

Waiting for device reboot

Wait about 45 seconds. IP monitor is now rebooting.

Check new AIPM configuration

Click on Refresh button to search IP monitor with new configuration.

Repeat this procedure for all IP monitors.

### Loading the actual version of the application

To load a new version of the application into the IP monitor is necessary to perform the following steps:

- Connecting to a FTP server of the IP monitor

- Deleting previous application files

- Copying of new application files

- Camera system restart

- Verifying of loaded application

In following procedure is used TotalCommander 7.5a for connection to FTP, but files can be loaded through any FTP client.

#### Connecting to a FTP server of the IP monitor

Launch the Total Commander and select from Main menu

Net --> FTP Connect

Total Commander – Main Menu

Click on the button New connection.. in dialog box Connect to ftp server.

TC – Connect to ftp server

Enter the parameters for connection to the first monitor (APPENDIX E – Configuration parameters, IP monitor):

Session name: 	Monitor_A

Host (Port): 		„AIPM_IP_A“

User name: 		„AIPM_Login“

Password: 		„AIPM_Password“

TC – FTP Connection details

Press the button Connect.

TC – Connection to Monitor_A

#### Deleting previous application files

Identify, in which files from connected monitor have been displayed (from heading bar - see figure), and delete them.

TC – Identification of FTP contents

#### Copying of new application files

Copy the new version of application.

Thanks to duration of copying process (typically 10 to 20 s), the communication seems „frozen“ for a short time. This behave is quite common. In case that „freezing“ takes several minutes, restart the camera system (power supply off and on) and repeat the procedure from the beginning of chapter 4.1.2 Loading the actual version of the application).

After completion of copying process press the „Disconnect“ button and repeat the same process for second monitor.

Parameters for connection to second monitor (APPENDIX E – Configuration parameters, IP monitor):

Session name: 	Monitor_B

Host (:Port): 		„AIPM_IP_B“

User name: 		„AIPM_Login“

Password: 		„AIPM_Password“

#### Camera system restart

Until restart of camera system has been done (power supply off and on) the new version of application does not manifest itself.

When no image appears on monitors after restart, loading of files were not performed properly. Possible reasons are:

- application version in monitors are different

- application files was corrupted

When it happens, load the application into both monitors again.

#### Verifying of loaded application

Application version is saved in the IP monitor in file app_apm.txt. File can be downloaded through FTP.

Connect to the monitor (Chapter 4.1.2  Connecting to a FTP server of the IP monitor).

View the app_apm.txt file content.

Application version can be detected from the text.

Verifying of application version

Verification must be performed for all monitors.

## AM3114A cameras commissioning

Commissioning of IP cameras consists of following steps:

- Camera identification

- Firmware upgrade

- Loading of configuration template

- Camera lens setup

##### Equipment needed

Service notebook.

axis_acm_200058 - Axis Camera Management (see Appendix D). ACM installation is described in Appendix C.

ks-630mil_am3114ra_cfg - configuration templates (see Appendix D).

Tool for dismounting of camera housing.

Tool for loosing of lens thread.

##### Initial state

Before start of camera installation is necessary to set camera system into following state:

- Powering of all components are switched off

- All cameras are disconnected from Ethernet

- Service PC with installed ACM is connected

- The database in ACM does not involve cameras connected before (otherwise they must be deleted – see chapter 4.2.4 Camera lens setup (positioning and focusing), section Deleting camera from ACM database).

Setting of service notebook network adapter:

IP address: 			“NB_IP_AXIS”

Subnet mask: 		“NB_MASK”

Default gateway: 		do not fill

### Camera identification

The first step is identification of particular camera. There are two scenarios available, which can be used for identification:

Cables are labelled near PoE switch – therefore cameras can be identified by connection.

#### Connect camera to Ethernet

Plug the Ethernet cable into the appropriate connector of particular camera and wait for about 30 s (time for camera start up).

#### Finding of connected camera through ACM

Launch the ACM on service PC and click on Search icon on Toolbar.

ACM – the Search icon

In the next dialog enter the value of „IP range“ for searching (APPENDIX E – Configuration parameters, IP address setting up) and confirm by OK button.

ACM – Network search dialog

If the search is unsuccessful and no camera is found, repeat this procedure.

Camera which has been found is shown in ACM Main window.

ACM – New camera is found

### Firmware upgrade

Select the camera by left mouse button click and launch the upgrading dialog by Upgrade button from Toolbar.

Upgrade button / icon

In the next dialog box click on <Select> and select M3114-R_5_40_9_2.bin file.

Selection of file with firmware

By checking the „Upgrade device in:“ radio button  we can affect the upgrade process, when a bulk upgrading of more cameras is made.

Parallel – cameras will be upgraded all at once

Sequence – cameras will be upgraded sequentially

Progress of upgrade process

Wait for upgrade completion.

Upgrade recapitulation

Finally, a recapitulation window is shown, which presents a list of upgraded cameras and results of upgrades.

### Loading of configuration template

Select the camera in ACM Main window by left mouse button click. Click on icon Apply Template on the Toolbar and the menu for selection of configuration template is displayed.

ACM – Looking for template

Through item Browse open a next window with list of configuration templates.

Selection of configuration template

Choose the configuration template, which is determined for connected camera.

Templates

After opening the configuration template a dialog box appears, that contains set of camera parameters which can be changed. Confirm this dialog by OK button and changes in setting the camera are applied.

Modified parameters

After applying of configuration template a recapitulation window is shown which contains result of loading and overview of all recently set parameters.

Recapitulation of changes performed in parameters

After pressing the Close button is configuration of camera parameters completed.

### Camera lens setup (positioning and focusing)

The whole process of setting the camera lens is realized in following steps:

- Viewing the image from camera on service notebook.

- Taking off the camera cover.

- Camera lens position setup

- Focusing the camera lens.

- Deleting camera from ACM database.

For mechanical adjusting of camera is used special tool composed of two parts: holder and the turning part.

Tool for adjusting lens

The turning part is used for:

- Focusing the camera lens.

- Position setting of head with lens.

#### Viewing the image from camera on service notebook

Setting of service notebook network adapter:

IP address: 			“NB_IP_CAM”

Subnet mask: 		“NB_MASK”

Default gateway: 		do not fill

Launch the internet browser on service notebook and enter into address field the IP address of camera, which will be focused / positioned.

Entering the camera IP address

Internet Explorer needs an ActiveX control for its operation. If not installed yet, you will be prompted to install it.

Installation of an ActiveX control

After installation is opened a login dialog, where login data for web access need to be entered:

User name: 	“CAM_Login”

Password: 	“CAM_Password”

Image from camera is displayed after click on Live View item, located in heading of web interface.

Launching of Live View

#### Taking off the camera cover

To remove the camera cover, two bolts which hold the cover must be released.

The bolts which hold the camera cover

Then, use a special plastic tool or flat screwdriver for lifting up and releasing the camera cover. If you had some resistance, you will need to use appropriate power.

Taking off the camera cover.

After removing the cover you can begin with lens position adjustment.

Legend to camera body

#### Camera lens position setup

Position of camera lens affects the image, which is captured by camera. Positioning is realized by turning the head with lens while the captured image is viewed over Live View on computer screen. Range of positioning is mechanically limited.

Camera lens positioning

When adjusting the camera lens in external housing is important to take into account the peephole through cover front side.

After adjusting the required lens position you can focus the camera image.

#### Focusing the camera lens

Camera is delivered with lens set by manufacturer. Therefore it is necessary to check the image quality, the lens must be focused as best as possible.

Focusing the camera lens

For focusing is used the same tool mentioned above. Turn the lens clockwise or counter clockwise while image sharpness is checked through Live View.

Pay a maximum attention to cleanliness of lens when turning it!

As soon as the focusing is completed, place the upper cover back on the camera.

#### Deleting camera from ACM database

After completion of procedures of camera configuration and lens adjusting is necessary to delete in ACM Main window records about cameras, with which it was worked.

The reason is, that there are application problems when cameras with the same IP address are repeatedly detected.

Records are deleted by following way:

- Disconnect the service computer from Ethernet

- Click on All Devices item in the left side of window, section Groups

- Click in the window central part, (where is the list of cameras) on camera and mark the all cameras (e.g. by Ctrl+A shortcut key)

- From Main Menu select the Edit / Delete From Database option

- Confirm the dialog „This will delete the selected device from the database. Continue?“ by pressing Yes button.

After confirming the previous dialog, in the left window side, section Groups will be displayed: All Devices (0)

## MD8562/B cameras commissioning

Commissioning of recording unit consists of following steps:

- IP address setting up

- Parameters setting up

- Camera lens setup

###### Equipment needed

Service notebook.

vivotek_iw2_11027 - Vivotek Installation Wizard 2 (see Appendix D).

ks-630mil_md8562b_cfg - configuration files (see Appendix D).

Setting of service notebook network adapter:

IP address: 			“NB_IP_CAM”

Subnet mask: 		“NB_MASK“

Default gateway: 		do not fill

### IP address setting up

Disconnect all Vivotek cameras from the ethernet network.

Install and run Vivotek Installation Wizard 2 (IW2).

IW2 start-up

Wait until IW2 finish network scan and then press Next button.

Device selection

Connect the first camera to the ethernet. Wait about 60 seconds and then press Refresh devices button.

You will see new connected camera. Select camera and (click by left mouse button) expand menu on left side of the IW2 window.

Manual Setup

Press Manual Setup button.

Password settings

In Administrator section do not set password, see the picture (if the password is set then delete them), and press Next button.

Network Type

Press No button.

IP address settings

Deselect “Get IP by DHCP Server automatically” and fill proper information about connected camera (APPENDIX E – Configuration parameters, Cameras).

IP address:		“KZ1“ / “KZ2“ / “KZ3 “/ “KZ4“

Sub net mask:	“CAM_MASK“

Default gateway	“CAM_GW”

Press Next button.

HTTP port settings

Check configuration and then press Next button.

Manual (Advanced)

HTTP port: 8080

DDNS Settings

Press Next button.

Mobile Access Setup

Press No button.

Apply settings

Press Apply button.

Progress bar

Wait until setting operation finish.

Apply settings status

Confirm information about successful IP set.

Access information

Check that IP on Access from Home: line is IP that you need. If do not, repeat setting procedure (sometimes IP is not changed). If IP is correct, press Exit button, disconnect camera, mark as prepared to parameters set and continue with next camera.

Make this setting for all Vivotek cameras and after that connect all Vivotek cameras to the network and proceed to next chapter.

### Parameters setting up

Connect all Vivotek cameras to the ethernet network, wait about 60 seconds and then run “run.bat” from the command line.

Parameters set

### Camera lens setup

Use the supplied screwdriver to detach the dome cover from the camera base.

Detach the dome cover

##### Viewing angle

Loosen the screws (not removing them) on the sides of lens module. Adjust the lens to a desired viewing angle When done, fasten the screws so that lens orientation can be fixed and withstand shock and vibration.

Viewing angle adjusting

##### Focus of the lens

The focus of this network camera is set from 1.0 m to infinity by factory default. If you want to focus on objects closer than 1.0 m or the lens has lost focus, please fine tune it in the following way.

Loosen the lens lock screw under the lens module. Manually rotate the lens to fine-tune the focus until the live image is clear.

Focus of the lens

Tighten the lens lock screw.

##### Completion

Tear down the aluminium foil vacuum bag and take out the moisture absorber. Attach the supplied moisture absorber to the inner side of the dome cover. (Please replace the absorber whenever you open the dome cover.)

Moisture absorber replacement

Attach the dome cover to camera. Secure the dome screws with the supplied screwdriver.

## Recording unit commissioning

Commissioning of recording unit consists of following steps:

- IP address setting up

- Check of power supply connector wiring

- Loading of actual version of an application

- Verifying version of loaded application

###### Equipment needed

Service notebook with installed FTP client (Total Commander is recommended).

ks-630mil_ppm21102t_app - application files (see Appendix D).

Setting of service notebook network adapter:

IP address: 			“NB_IP_PPM”

Subnet mask: 		“NB_MASK“

Default gateway: 		do not fill

### Check of power supply connector wiring

Checking of proper wiring of recording unit powering is necessary before the first unit switching on.

For switching the unit off must be essentially used the terminal labelled SB. Terminal with label +U should be connected permanently to vehicle battery.

Recording unit power supply wiring

Only such wiring ensures the faultless unit operation.

###### SB function

| SB | Device state |
| --- | --- |
| +U | Device is ON |
| not connected | Device is OFF |

While disconnecting SB, sequence of steps for system turn-off is started. When signal SB is disconnected, the auxiliary CPU sends to main CPU a turning-off signal

Immediately after successful main CPU turn-off, the whole Recording Unit is disabled. If the main CPU is not switched off due to failure, Recording Unit is after 1 minute switched off automatically.

Disconnecting of supplying conductors is done only after previous Recording Unit switching-off through SB signal. If not, you may lose data.

### IP address setting up

Connect only one recording unit to the ethernet network. Connect service notebook to vehicle ethernet and turn-off firewall.

Run AmitDeviceDetection.exe and wait until ethernet scan finish.

Searching for AMiT devices

AmitDeviceDetection will find connected recording unit. If you have connected IP monitors, you will see them also.

Recording unit has been found

Click right mouse button on recording unit and select Change IP settings.

IP settings dialog

IP Settings dialog will appears. Set IP address of the connected recording unit (APPENDIX E – Configuration parameters, Recording unit) and press OK button.
	IP address: 			“RU_IP_A” or “RU_IP_B”

Subnet mask: 		“RU_MASK”

New IP settings

Now you will see recording unit with new IP address. Disconnect configured  recording unit and repeat for other recording units.

### Loading the actual version of an application

To load a new version of an application into recording unit is necessary to perform the following steps:

- Connecting to a FTP server of the recording unit

- Deleting previous application files

- Copying of new application files

- Restart recording unit

- Verifying of loaded application

In following procedure is used TotalCommander 7.5a for connection to FTP, but files can be loaded through any FTP client.

#### Connecting to a FTP server of the recording unit

Launch the Total Commander and select from Main menu

Net --> FTP Connect

Total Commander – Main Menu

Click on the button New connection.. in dialog box Connect to FTP server

TC – Connect to ftp server

Enter the parameters to connect to recording unit (APPENDIX E – Configuration parameters, Recording unit):

Session name: 	RU

Host (Port): 		„RU_A_IP“ or „RU_B_IP“

User name: 		„RU_Login“

Password: 		„RU_Password“

TC – Monitor_A – parameters

Press the button Connect.

TC – Connection to recording unit

#### Deleting previous application files

Identify, in which tab are displayed files from connected monitor (from heading bar - see figure).

TC – Identification of FTP contents

Delete the app directory. If there is no app directory, proceed to next step.

#### Copying of new application files

Copy the app directory with new version of application according to APPENDIX D – Program set.

TC – Disconnect from FTP

After completion of copying process press the Disconnect button.

#### Recording unit restart

Turn recording unit off and on. Before next start hard drive will be formatted. It takes approximately five minutes.

#### Verifying of loaded application

Version of application, which is loaded in Recording unit, you can get from response to http request info.

Run the internet browser (Firefox or Chrome recommended).

Enter the command <ru_ip>:8888/info (e. g. 10.10.1.120:8888/info for recording unit with ip address 10.10.1.120) into the line for address setting

Confirm the command by Enter key.

As response to sent request the browser displays a xml file.

Version number is available between two tags

<version>........</version>

Identification of application version

## ERT03/A2 commissioning

Commissioning of router ERT03/A2 consists of following steps:

- Update from ERT/A1 to ERT/A2

- Parameters setting up

##### Equipment needed

Service notebook.

ks-630mil_ert03a2_app - application files (see Appendix D).

ks-630mil_ert03a2_cfg - configuration files (see Appendix D).

### Update from ERT/A1 to ERT/A2

Setting of service notebook network adapter:

IP address: 			“NB_IP_ERT”

Subnet mask: 		“NB_MASK“

Default gateway: 		do not fill

Connect notebook to the ECN network of commisioned router.

Run ert03a2_cms_xxx.bat from the command line. Follow on screen instructions.

### Parameters setting up

Setting of service notebook network adapter:

IP address: 			“NB_IP_CAM”

Subnet mask: 		“NB_MASK“

Default gateway: 		do not fill

Connect notebook to the ECN network of commisioned router.

Run ert03a2_cfg_xxx.bat from the command line. Follow on screen instructions.

### Application update

If you are already using ERT03/A2 and what you only need is an update of the application.

Setting of service notebook network adapter:

IP address: 			“NB_IP_CAM”

Subnet mask: 		“NB_MASK“

Default gateway: 		do not fill

Connect notebook to the ECN network of commisioned router.

Run ert03a2_app_xxx.bat from the command line. Follow on screen instructions.

# APPENDIX A – Location of components

# APPENDIX B – Scenes

| Scene ID | Stream from camera | Symbol |
| --- | --- | --- |
| 0 | no stream | none – black screen |
| 1 | KW1 | KW1 |
| 2 | KW2 | KW2 |
| 3 | KW3 | KW3 |
| 4 | KW4 | KW4 |
| 5 | KW5 | KW5 |
| 6 | KW6 | KW6 |
| 7 | KW7 | KW7 |
| 8 | KW8 | KW8 |
| 9 | KW9 | KW9 |
| 10 | KW10 | KW10 |
| 11 | KW11 | KW11 |
| 12 | KW12 | KW12 |
| 13 | KZ1 | KZ1 |
| 14 | KZ2 | KZ2 |
| 15 | KZ3 | KZ3 |
| 16 | KZ4 | KZ4 |
| 17 | KS1 | KS1 |
| 18 | KS2 | KS2 |
| 19 | KW1[2] | KW1[2] |
| 20 | KW2[2] | KW2[2] |
| 21 | KW3[2] | KW3[2] |
| 22 | KW4[2] | KW4[2] |
| 23 | KW5[2] | KW5[2] |
| 24 | KW6[2] | KW6[2] |
| 25 | KW7[2] | KW7[2] |
| 26 | KW8[2] | KW8[2] |
| 27 | KW9[2] | KW9[2] |
| 28 | KW10[2] | KW10[2] |
| 29 | KW11[2] | KW11[2] |
| 30 | KW12[2] | KW12[2] |
| 31 | KZ1[2] | KZ1[2] |
| 32 | KZ2[2] | KZ2[2] |
| 33 | KZ3[2] | KZ3[2] |
| 34 | KZ4[2] | KZ4[2] |
| 35 | KS1[2] | KS1[2] |
| 36 | KS2[2] | KS2[2] |
| 37 | KW1[3] | KW1[3] |
| 38 | KW2[3] | KW2[3] |
| 39 | KW3[3] | KW3[3] |
| 40 | KW4[3] | KW4[3] |
| 41 | KW5[3] | KW5[3] |
| 42 | KW6[3] | KW6[3] |
| 43 | KW7[3] | KW7[3] |
| 44 | KW8[3] | KW8[3] |
| 45 | KW9[3] | KW9[3] |
| 46 | KW10[3] | KW10[3] |
| 47 | KW11[3] | KW11[3] |
| 48 | KW12[3] | KW12[3] |
| 49 | KZ1[3] | KZ1[3] |
| 50 | KZ2[3] | KZ2[3] |
| 51 | KZ3[3] | KZ3[3] |
| 52 | KZ4[3] | KZ4[3] |
| 53 | KS1[3] | KS1[3] |
| 54 | KS2[3] | KS2[3] |
| 55 | KW1, KW2, KW3, KW4 | KW1, KW2, KW3, KW4 |
| 56 | KW5, KW6, KW7, KW8 | KW5, KW6, KW7, KW8 |
| 57 | KW9, KW10, KW11, KW12 | KW9, KW10, KW11, KW12 |
| 58 | KZ1, KZ2 | KZ1, KZ2 |
| 59 | KS1, KS2 | KS1, KS2 |
| 60 | KW12, KW11, KW10, KW9 | KW12, KW11, KW10, KW9 |
| 61 | KW8, KW7, KW6, KW5 | KW8, KW7, KW6, KW5 |
| 62 | KW4, KW3, KW2, KW1 | KW4, KW3, KW2, KW1 |
| 63 | KZ4, KZ3 | KZ4, KZ3 |
| 64 | KS2, KS1 | KS2, KS1 |

##### Default setting

| Scene ID | Stream from camera | Symbol |
| --- | --- | --- |
| 0 | No stream | none – black screen |

# APPENDIX C – Block diagram

# APPENDIX D – Program set

Actual program set: 130725_KS-630MiL

Download link:

http://imp.amit.cz/www/kamerove_systemy/pesa/630mil/index.html

#### IP monitor - AIPM1013/A

| Directory | File | Description |
| --- | --- | --- |
| ks-630mil_aipm1013a_app_2015 | app_apm.conf | Configuration file |
|  | app_apm.sh | Starting script |
|  | app_apm.txt | Version file |
|  | app_apm.tar.gz | Application |
| ks-630mil_aipm1013a_cfg_101 | ALBDConfig.exe | Configuration tool |
|  | albdconfig.xml | Configuration file |

#### Camera - AM3114-R/A

| Directory | File | Description |
| --- | --- | --- |
| ks-630mil_am3114ra_cfg_202 | ks-630mil_ks1_v2.02.cmt | Config. template KS1 |
|  | ks-630mil_ks2_v2.02.cmt | Config. template KS2 |
|  | ks-630mil_kw1_v2.02.cmt | Config. template KW1 |
|  | ks-630mil_kw2_v2.02.cmt | Config. template KW2 |
|  | ks-630mil_kw3_v2.02.cmt | Config. template KW3 |
|  | ks-630mil_kw4_v2.02.cmt | Config. template KW4 |
|  | ks-630mil_kw5_v2.02.cmt | Config. template KW5 |
|  | ks-630mil_kw6_v2.02.cmt | Config. template KW6 |
|  | ks-630mil_kw7_v2.02.cmt | Config. template KW7 |
|  | ks-630mil_kw8_v2.02.cmt | Config. template KW8 |
|  | ks-630mil_kw9_v2.02.cmt | Config. template KW9 |
|  | ks-630mil_kw10_v2.02.cmt | Config. template KW10 |
|  | ks-630mil_kw11_v2.02.cmt | Config. template KW11 |
|  | ks-630mil_kw12_v2.02.cmt | Config. template KW12 |
|  | M3114-R_5_40_9_2.bin | Firmware |
| axis_acm_200058 | axis_acm_2.00.058.exe - | Installation file |

#### Camera - MD8562/B

| Directory | File | Description |
| --- | --- | --- |
| ks-630mil_md8562b_cfg_102 | run.bat | Configuration script |
|  | client.lua | Configuration file |
| vivotek_iw2_11027 | IW2_Setup.exe | Installation file |
|  | IW2_V1.1.0.27_release_note.txt | Version file |

#### Router - ERT03/A2

| Directory | File | Description |
| --- | --- | --- |
| ks-630mil_ert03a2_app_120 | ert3-a2_a_120.bin | Application file |
|  | ert03a2_app_120.bat | Download script |
|  | ert03a2_cms_120.bat | Download script |
|  | ERT03A2_Config.exe | Configuration tool |
| ks-630mil_ert03a2_cfg_100 | ert03a2_cfg_100.bat | Configuration script |
|  | ERT03A2_Config.exe | Configuration tool |

#### Acasys Studio Vehicle Profile

| Directory | File | Description |
| --- | --- | --- |
| - | ks-630mil_Vehicle Profile_101.exe | Installation file |

#### Recording unit - PPM2110/2T

| Directory | File | Description |
| --- | --- | --- |
| ks-630mil_ppm21102t_app_30r39 /A/app | app.conf | Configuration file |
|  | app.md5 | Checksum file |
|  | app.tar.gz | Application |
|  | app.txt | Version file |
|  | controller.conf | RU1 (A) - control config. |
| ks-630mil_ppm21102t_app_30r39 /B/app | app.conf | Configuration file |
|  | app.md5 | Checksum file |
|  | app.tar.gz | Application |
|  | app.txt | Version file |
| ks-630mil_ppm21102t_ios_1040 | ppm21xx_ios_1040.img | OS image file |
|  | img2usb.exe | Image burner |
| AmitDeviceDetection_104 | AmitDeviceDetection.exe | Configuration tool |

# APPENDIX E – Configuration parameters

In following tables are presented parameters, which serves for working with camera system or which are used for configuration and service operations.

For several parameters is used a Symbolic name system. The symbolic name is in previous chapters represented as „Symbolic name“. Instead of this name in described operation is necessary to enter a Value, which is presented in tables below.

## IP address setting up

| Symbolic name | Value |
| --- | --- |
| IP_Range | 192.168.0.* |
| NB_IP_AIPM | 10.10.1.33 |
| NB_IP_PPM | 10.10.1.33 |
| NB_IP_AXIS | 192.168.0.33 |
| NB_IP_CAM | 10.10.1.33 |
| NB_IP_ERT | 192.168.1.33 |
| NB_MASK | 255.255.0.0 |

## Cameras

Overview of parameters referring to camera adjusting.

| Camera | IP Address | Location | Configuration template |
| --- | --- | --- | --- |
| KS1 | 10.10.1.121 | int. track, cabin A | ks-630mil_ks1_vx.xx.cmt |
| KS2 | 10.10.1.122 | int. track, cabin B | ks-630mil_ks2_vx.xx.cmt |
| KW1 | 10.10.1.123 | int. passengers | ks-630mil_kw1_vx.xx.cmt |
| KW2 | 10.10.1.124 | int. passengers | ks-630mil_kw2_vx.xx.cmt |
| KW3 | 10.10.1.125 | int. passengers | ks-630mil_kw3_vx.xx.cmt |
| KW4 | 10.10.1.126 | int. passengers | ks-630mil_kw4_vx.xx.cmt |
| KW5 | 10.10.1.127 | int. passengers | ks-630mil_kw5_vx.xx.cmt |
| KW6 | 10.10.1.128 | int. passengers | ks-630mil_kw6_vx.xx.cmt |
| KW7 | 10.10.1.129 | int. passengers | ks-630mil_kw7_vx.xx.cmt |
| KW8 | 10.10.1.130 | int. passengers | ks-630mil_kw8_vx.xx.cmt |
| KW9 | 10.10.1.131 | int. passengers | ks-630mil_kw9_vx.xx.cmt |
| KW10 | 10.10.1.132 | int. passengers | ks-630mil_kw10_vx.xx.cmt |
| KW11 | 10.10.1.133 | int. passengers | ks-630mil_kw11_vx.xx.cmt |
| KW12 | 10.10.1.134 | int. passengers | ks-630mil_kw12_vx.xx.cmt |
| KZ1 | 10.10.1.135 | ext. left, cabin A | ks-630mil_md8562b_cfg_xxx |
| KZ2 | 10.10.1.136 | ext. right, cabin A |  |
| KZ3 | 10.10.1.137 | ext. left, cabin B |  |
| KZ4 | 10.10.1.138 | ext. right, cabin B |  |

#### Login data

| Symbolic name | Value |
| --- | --- |
| CAM_Login | root |
| CAM_Password | pass |

#### Network settings

| CAM_GW | 10.10.1.254 |
| --- | --- |
| CAM_MASK | 255.255.0.0 |

## IP monitor

Overview of parameters which refers to IP monitor adjusting.

| Symbolic name | IP monitor | Value |
| --- | --- | --- |
| AIPM_IP_A | IP monitor A | 10.10.1.139 |
| AIPM_IP_B | IP monitor B | 10.10.1.140 |
| AIPM_Login | - | service |
| AIPM_Password | - | remote |

## Recording unit

Overview of parameters referring to Recording unit adjusting.

| Symbolic name | Value |
| --- | --- |
| RU_IP_A | 10.10.1.119 |
| RU_IP_B | 10.10.1.120 |
| RU_MASK | 255.255.0.0 |
| RU_Login | service |
| RU_Password | remote |

# Appendix F – Axis Camera Management (ACM)

For detection of cameras and configuration of their parameters is used an effective installation and management tool for IP cameras - Axis Camera Management version 2.00 (in this document referred as ACM).

Axis Camera Management - Main window

##### Link to download

ACM can be downloaded from Axis company website. Direct link to download (verified to date 2012.08.23):

http://www.axis.com/products/cam_mgmt_software/index.htm

Download is conditioned by free of charge registration.

#### Installation

Does not require any special settings All options can be default.

#### First start – password setup

At the first launch is automatically activated the Set Master Credentials dialog box.

Master Credentials setting

User name and Password will be used afterwards for accessing cameras, therefore they need to be set in accordance with APPENDIX E – Configuration parameters, Login data:

User name: 		„CAM_Login“

Password: 		„CAM_Password“

Access: 		checked

# Appendix G – IP cameras

#### Operation thru web interface of the camera

Besides automatic configuration via ACM can be camera parameters changed also through web configuration interface, which each Axis camera contains.

###### Warning:

Any intervention to camera configuration (except for actions described below) are not recommended. They can affect negatively the image quality and camera performance.

The procedures described below assume that we are working with the camera, which has its IP address already assigned.

#### Description of web interface window

The web interface window can be divided into three parts:

Heading – toggling of Parameterization section (Live View / Setup) and viewing of context help

- Live View – live image from camera

- Setup – parameters setting

Left side menu – navigation in Parameterization section parameters

Parameterization section – performing of service operations and changing of settings

Description of web interface window

#### Web interface login

All operations described in following chapters require previous separate web interface login.

Launch the internet browser (Internet Explorer is recommended) and enter into address field an IP address of camera, web interface of which you want to view.

Entering of camera IP address

Internet Explorer needs an ActiveX control for its operation. If not installed yet, you will be prompted to install it.

ActiveX control enabling.

After installation is opened a login dialog, where login data for web access need to be entered:

User name: 	„CAM_Login“

Password: 	„CAM_Password“

Web interface login dialog

After login, an entry site of web interface is displayed. Click on Setup item in web interface Heading.

Displaying of parameters setting

#### Live View – live image from camera

Image from camera is displayed after click on Live View item, located in web interface Heading.

Displaying of live image from camera

#### Creating of Server Report

In starting screen select the section System Options in Left menu.

System Options section

Then, proceed into subsections:

Support ( Logs & Reports ( Information.

Navigation in System Options section

Generate the Server Report by click on appropriate button. Then it will be available in right - Parameterization - window part.

Generating of Server Report

Finally, new dialog window appears, where is shown the Server Report, which can be copied into text file and sent for analysis..

View on Server Report

## Restoring the factory setting

You can restore the original factory setting. It can be done by two ways:

- By software way – restores the factory setting of parameters including/ with exception of (optionally) Ethernet interface.

- By hardware way – factory setting of all parameters.

After resetting is the camera considered as quite new and next steps can be performed in accordance with 4.2 AM3114A cameras commissioning.

#### Software way of Restoring the factory setting

Login to camera web interface (see Appendix G – IP cameras, Web interface login).

In starting screen select the section System Options and Maintenance sub-section in Left menu.

Factory settings through software - menu

Screen with several buttons is displayed. Their meaning is evident from labels.

Software way of Restoring the factory setting

Restore – IP address is retained, all another parameters are reseted.

Default – all parameters including IP address are restored.

After click on one of these buttons and confirming in dialog box the camera „freezes“ for several tens of seconds (camera restart is part of all operations).

#### Hardware way of Restoring the factory setting

When happens that even by using the ACM the camera cannot be found in network and you are 100 % sure that camera is properly connected into network, then the hardware reset into factory setting is recommended.

Resetting of all parameters including IP address:

- Disconnect the camera network cable

- Dismount the camera cover

To remove the camera cover, two bolts which holds the cover must be released.

The bolts which holds the camera cover

Then, use a special plastic tool or flat screwdriver for lifting up and releasing the camera cover. An appropriate power needs to be applied due to some resistance.

Taking off the camera cover.

Legend to camera body

- Press and hold the Control button, attach the network cable.

- Hold the Control button and wait until LED Status indicator starts light yellow (it can take up to 15 seconds).

- Release the Control button. When the LED Status indicator starts light green (it can take up to 1 minute), process is completed an camera is reseted.

- Perform the camera configuration according to 4.2 AM3114A cameras commissioning.

## Meaning of camera LED indicators

| LED | Colour | Description |
| --- | --- | --- |
| NET | Green | Connected to 100 Mbit/s network. Blinking indicates the network activity. |
|  | Orange | Connected to 10 Mbit/s network. Blinking indicates the network activity. |
|  | Does not light | Not connected to network. |
| STAT | Green | Camera runs and is OK. |
|  | Orange | Camera start / reset to factory setting is under way. |
|  | Red | Blinks slowly after unsuccessful firmware upgrade. |
| PWM | Green | Power supply is attached. |
|  | Orange | Blinks green/orange when firmware upgrade is under way. |
|  | Does not light | Camera is not powered. |

# Appendix H - Recording unit OS update

Appendix describes how to update operating system of recording unit. Update is made via USB flash disc.

OS update consists of following steps:

- Create bootalbe USB flash disk

- Run recording unit from USB flash disk

##### Equipment needed

Service notebook.

USB flash disc with minimal capacity 4 GB.

USB flash disc image ks-630mil_ppm21102t_ios (see Appendix D).

## Create bootalbe USB flash disk

Plug in clear the USB flash disc to the service notebook.

Open Start menu and

- click right mouse button on „My Computer“ and from context menu chose  „Manage->Disc Management“

- in Disc Management identify connected USB flash disc

Disc management

Delete all partitions on USB flash disc:

- click right mouse button on USB flash disc partition

- chose Delete partition from context menu”

Delete partition

Confirm partition delete by click Yes.

Disc management - warning

Repeat for all USB flash disc partitions.

USB flash disc without partitions

Open a command prompt as Administrator. Navigate to directory with USB flash disc image and img2usb.exe tool.

Directory selection

Run img2usb tool:

img2usb.exe <usb flash disc file>

Run img2usb.exe tool

Enter the number of the connected USB flash disc to write image.

Disc selection

Check that you choose the right disc and confirm your selection.

Disc confirmation

Do not make any write operation to created USB flash disc and wait until operation is finished!

Image writing in progress

USB flash disc is ready to use.

Img2usb.exe – successfully written

Safely remove USB flash disc from service notebook.

## Run recording unit from USB flash disk

Switch off the recording unit.

Plug in the USB flash disk to USB connector on recording unit.

Switch on the recording unit, this is indicated with short low beeb.

Wait a few seconds until the unit boot up.

When update procedures starts, you will hear periodic beep with low/high tone.

During uploading of operating system, you will hear low tone with 4 s gap.

When update procedure ends correctly, you will hear loud melody whitch ends with high tone.If not, you will hear melody whitch ends with low tone.

Po dokončení všech operací (může proběhnot kontrola disku) následuje závěrečná melodie.

Switch off the recording unit.

Disconnect the USB flash disk.

Switch on the recording unit.

## Verifying version of OS

Version of OS which is loaded in recording unit you can get from the web interface.

###### Procedure

Adjust the fixed IP address to service notebook network adapter:

IP Address: 			„NB_IP_PPM“

Subnetwork mask: 		„NB_MASK“

Gateway: 			do not fill

Launch the Internet browser (e.g. Internet Explorer).

Enter the https://<ru_ip> adress into the address field (for example https://192.168.20.120 for recording unit with IP address 192.168.20.120).

Confirm the adress by Enter key.

OS version

In opening window you can see version of loaded OS.

# Text boxes

Version 1.02

Assembly manual

Camera system