10M Ethernet

# PCMCIA Adapter

# Users' Guide

## Introduction

Congratulations on your purchase of the 10M Ethernet PCMCIA Adapter.  This users' guide is provided to allow you to get the most out of your new investment.   It describes all featurs and covers installation and operating instructions of the 10M Ethernet PCMCIA Adapter in an easy-to-read yet thorough manner.

## Package Contents

?One 10M Ethernet PCMCIA Adapter

?One media coupler:

Type 1: PCMCIA Adapter with RJ-45 and one BNC

connectors

Type 2: PCMCIA Adapter with one RJ-45 connector only

?One driver diskette

?This Users' Guide

### Feature Overview

Your 10M Ethernet PCMCIA Adapter includes the following features:

Standards: IEEE 802.3, PCMCIA release 2.1, JEIDA 4.1

PCMCIA Type II card (PC Card)

Novell NE2000 and Card Master compatible

PC Card: approximately credit card size

Switchless configuration and operation

Software configurable

Full support for PCMCIA Card Information Structure (CIS)

and low power consumption

16-bit bus interface and 32KB network packet buffer

Two Diagnostic indicators (on media coupler)

1

# The Ethernet Adapter

The 10M Ethernet PCMICA adapter consists primarily of two parts: the PCMCIA network card and the media coupler. It is a PCMCIA type II card and equipped with two connectors, one at each end of the card.

68-Pin Connector

The 68-pin connector is used to insert into the computer's PCMCIA slot.

This connector interfaces with the computer.

Label

The label must be facing up while inserting the card into the slot.

15-Pin Flat Connector

Use to connect the adapter to the media coupler.

The media coupler is used to make the connection with the network.

Type 1 PCMCIA Adapter

2

]

Type 2 PCMCIA Adapter

Activity (ACT) Indicator

This LED lights green when a network is sending or receiving data

Link (LINK) Indicator

This LED lights green when a 10BASE-T network connection has been established with the RJ-45 connector. This indicator has no effect (does not light) when using the BNC connector with a 10BASE2 network.

BNC Network Connector

This connector is used to link the adapter to a 10BASE2 network.

RJ-45 Network Connector

This connector is used to link the adapter to a 10BASE-T network.

3

5-Year Warranty

The manufacturer warrants to the original consumer /purchaser free from defects in materials or workmanship for limited time from the original factory shipment date.

KEEP THIS STUB FOR YOUR RECORDS

Model:                                  Serial :

Date Purchased:

Where Purchased:

From Whom:

MANUFACTURER                 DISTRIBUTOR

5-Year Warranty

TO:

ATTN:

WARRANTY REGISTRATION CARD

Please complete this form and return it within 10 days of purchase to validate warranty

Name/Title:

Company:

Address:

Tel. No.:			Signature:

Purchase Model:                    Serial No.:

Purchase from:

Address:

Date of Purchase:

4

Federal Communications

Commission Statement

This equipment generates, uses, and can radiate rad frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communications.  This equipment has been tested and found to comply with the limits for a class A computing device, pursuant to Part 15 of the FCC rules. These limits are designed to provide reasonable protection against harmful interference when operated in a commercial environment.  Operation of this equipment in a residential area is likely to cause interference, in which case the user, at his own expense, will be required to take whatever measures are necessary to correct the interference.

CE Declaration of conformity

This equipment complies with the requirements relating to electromagnetic compatibility, EN 55022 class A for ITE and EN 50082-1.  This meets the essential protection requirements of the European Council Directive 89/336/EEC on the approximation of the laws of the Member States relating to electromagnetic compatibility.

Trademarks

Ethernet is a trademark of Xerox Corporation. IBM, PC/XT/AT are trademarks of International business Machines Corporation. NE2000, NE2000T and NetWare are trademarks of Novell Corporation. Microsoft and MS-DOS are registered trademarks of Microsoft Corporation. Windows is a trademark of the Microsoft Corporation. Other trademarks are the properties of their respective holders.

5

Hardware Installation

Follow the steps listed below to install the 10M Ethernet adapter and media coupler.

Step 1:	Unpack the10M Ethernet PCMCIA Adapter

Step 2:	Switch off your computer's power.

Step 3:	Locate an available PCMCIA slot.

Step 4:	Insert the 10M Ethernet PCMCIA Adapter

card into the available slot type II slot.

Step 5:	Connect the media coupler to the PC Card's 15-pin connector.

Step 6A:For 10BASE-T Networks.

Connect one end of the straight UTP cable to the RJ-45 connector on the media coupler.  Connect the other end of the cable to a 10BASE-T hub.  Illustrated as Figure A below.

Step 6B:For 10BASE2 Networks.

Connect a BNC T-connector coupler's BNC connector. Connect the 10BASE2 thin coaxial cables to the two open ends of the BNC T-connector. Illustrated as Figure B below.

Step 7: 	Turn on the computer containing the card and media coupler.

Figure A: 10 BASE-T Network Connection

6

Figure B:  10BASE 2 Network Connection

Now the10M Ethernet PCMCIA Adapter adapter  is installed and ready to be configured using the Setup Program provided on the diskette.

Software Setup

The 10M Ethernet PCMICA Adapter employs an innovative setup utility program for setting all configuration options.  Please refer to the README.DOC file found on the diskette provided for instructions on how to run the setup program.

README File

Updates to this user guide are described in the README.DOC file found on the diskette provided.  Please take a few minutes to print and read this file so that you don't miss any important changes to this guide.

7