MAMC-XLINK

Technical Reference Manual V1.0

HW Revision 1.0, 1.1

The MAMC-XLINK has been designed by:

Meikon Ltd
10 Bringsty Common
Worcester
WR6 5UJ

Great Britain

Phone +44 1886 822208
Internet: http://www.meikon.net

and

N.A.T. GmbH

Kamillenweg 22

53757 Sankt Augustin

Germany

Phone: +49 2241 3989-0

Fax: +49 2241 3989-10

E-Mail: support@nateurope.com

Internet: http://www.nateurope.com

Disclaimer

The following documentation, compiled by Meikon Ltd. and N.A.T. GmbH (henceforth called Meikon and N.A.T.), represents the current status of the product´s development. The documentation is updated on a regular basis. Any changes which might ensue, including those necessitated by updated specifications, are considered in the latest version of this documentation. Meikon and N.A.T. are under no obligation to notify any person, organization, or institution of such changes or to make these changes public in any other way.

Caution this publication may include technical inaccuracies or typographical errors.

Meikon and N.A.T. offer no warranty, either expressed or implied, for the contents of this documentation or for the product described therein, including but not limited to the warranties of merchantability or the fitness of the product for any specific purpose.

In no event will Meikon or N.A.T. be liable for any loss of data or for errors in data utilization or processing resulting from the use of this product or the documentation. In particular, Meikon or N.A.T. will not be responsible for any direct or indirect damages (including lost profits, lost savings, delays or interruptions in the flow of business activities, including but not limited to, special, incidental, consequential, or other similar damages) arising out of the use of or inability to use this product or the associated documentation, even if Meikon or N.A.T., or any authorized representative has been advised of the possibility of such damages.

The use of registered names, trademarks, etc. in this publication does not imply, even in the absence of a specific statement, that such names are exempt from the relevant protective laws and regulations (patent laws, trade mark laws, etc.) and therefore free for general use. In no case does Meikon or N.A.T. guarantee that the information given in this documentation is free of such third-party rights.

Neither this documentation nor any part thereof may be copied, translated, or reduced to any electronic medium or machine form without the prior written consent from Meikon or N.A.T..

This product (and the associated documentation) is governed by the Meikon and N.A.T. General Conditions and Terms of Delivery and Payment.

Table of Contents

List of Tables	5

List of Figures	5

Conventions	6

1	Introduction	7

1.1	Installation	8

1.2	Block Diagram	9

1.3	Board Features	10

1.4	Board Specification	11

2	Installation	12

2.1	Safety Note	12

2.2	Installation Prerequisites and Requirements	13

2.2.1	Requirements	13

2.2.2	Power supply	13

2.2.3	Automatic Power Up	13

2.2.4	Thermal Considerations	13

2.3	Statement on Environmental Protection	14

2.3.1	Compliance to RoHS Directive	14

2.3.2	Compliance to WEEE Directive	14

2.3.3	Compliance to CE Directive	15

2.4	Location Overview	16

3	Functional Blocks	17

3.1	Re-Driver Circuitry	17

3.2	IPMI Controller	17

3.3	IPMB Interface	17

3.4	AMC Clock Interface	18

3.5	Cable Interface Control Signals	18

4	Hardware Description	19

4.1	AMC Port Definition	19

4.2	Definition of ATmega645 Port Pins	20

4.3	Front Panel LEDs	22

4.3.1	AMC Standard LEDs	22

4.3.2	4 LED Block	22

5	Connectors and Switches	23

5.1	Connector Overview	23

5.2	AMC Connector CON1	24

5.3	Front Panel Connector CON2	26

5.4	AVR Programming Port Connector JP1	26

5.5	Hot Swap Switch SW1	27

5.6	DIL Switch SW2	27

5.7	DIL Switch SW3	27

6	MAMC-XLINK Programming Notes	28

6.1	AMC Control Signals	28

6.2	Selecting the PCIe Clock Source	28

6.3	PCI Express External Cable Interface Control Signals	28

6.4	Programming the Re-Driver Device Strapping Pins	29

6.4.1	Re-Driver Strapping Pins Description	29

6.5	Setup of the Serial Interfaces	30

6.5.1	I2C Interfaces	30

6.5.2	SPI Interface	30

7	Known Bugs / Restrictions	31

Appendix A: Reference Documentation	32

Appendix B: Document’s History	33

List of Tables

Table 1:	List of used Abbreviations	6

Table 2:	MAMC-XLINK Features	11

Table 3:	AMC Port Definition	19

Table 4:	ATmega645 Port Pin Usage (Port A)	20

Table 5:	ATmega645 Port Pin Usage (Port B)	20

Table 6:	ATmega645 Port Pin Usage (Port C)	20

Table 7:	ATmega645 Port Pin Usage (Port D)	21

Table 8:	ATmega645 Port Pin Usage (Port E)	21

Table 9:	ATmega645 Port Pin Usage (Port F)	21

Table 10:	ATmega645 Port Pin Usage (Port G)	22

Table 11:	AMC Connector CON1	24

Table 12:	Pin Assignment of the Front Panel Connector CON2	26

Table 13:	ATmega645 Programming Port JP1	26

Table 14:	Switch Assignment of DIL Switch SW2	27

Table 15:	Switch Assignment of DIL Switch SW2	27

Table 16:	Re-Driver Strapping Pins SEL0 – 2, Equalizer Selection	29

Table 17:	Re-Driver Strapping Pins SEL3 – 4, Output Swing Control	29

Table 18:	Re-Driver Strapping Pins SEL5 – 6, Output De-emphasis Adjustment	29

List of Figures

Figure 1:	MAMC-XLINK on a Carrier Board (ATCA)	8

Figure 2:	MAMC-XLINK Block Diagram	9

Figure 3:	Location Diagram of the MAMC-XLINK	16

Figure 4:	Connectors of the MAMC-XLINK	23

Conventions

If not otherwise specified, addresses and memory maps are written in hexadecimal notation, identified by 0x.

Table 1 gives a list of the abbreviations used in this document:

List of used Abbreviations

| Abbreviation | Description |
| --- | --- |
| AMC | Advanced Mezzanine Card |
| ATCA | Advanced Telecommunications Computing Architecture |
| b | Bit, binary |
| B | byte |
| IPMI | Intelligent Platform Management Interface Specification |
| MCH | µTCA Carrier Hub |
| µTCA | Micro Telecommunications Computing Architecture |
| nc | not connected |
| PCI | Peripheral Component Interconnect |
| PCIe | PCI Express |
| PICMG | PCI Industrial Computer Manufacturers Group |

# Introduction

The MAMC-XLINK is a high performance standard Advanced Mezzanine Card, single width, full height. It can be plugged onto any ATCA carrier board supporting AMC standards. It is also designed to meet the requirements of µTCA systems.

The MAMC-XLINK connects one lane of a PCIe backplane through a programmable Re-Driver circuitry to a PCI Express External Cable Interface Connector on the front panel.

The MAMC-XLINK is member of a family of XLINK boards which enable the connection of different system platforms via a PCI Express External Cable Interface. Typically one system will be a master system containing a processor card and the second system will be a slave system which does not contain a processor card and is controlled by the master system. Examples of other XLINK products are the MPCI-XLINK and the MPCIe-XLINK.

## Installation

The MAMC-XLINK can be installed either on a carrier board or plugged into a µTCA system.

MAMC-XLINK on a Carrier Board (ATCA)

The MAMC-XLINK provides master functionality for the cable interface, i.e. provides clock and management signals. When connecting it to another XLINK board, please make sure that the other board does not have master functionality for the cable interface. The other board will be in a slave system. This slave system should be powerd up before the system containing the MAMC-XLINK to ensure that the AMC system finds the slave rack when it powers up.

## Block Diagram

The MAMC-XLINK has the following major features implemented on-board:

- 1 Lane PCI Express Interface Rev. 1.1 to backplane

- 1 Lane PCI Express External Cable Interface Rev. 1.0 to front panel

- Re-Driver circuitry for boost and reshaping of the PCIe signals

- IPMI Controller

MAMC-XLINK Block Diagram

## Board Features

- PCI Express Interface

The MAMC-XLINK includes a 1 – lane PCI Express interface. The PCI Express interface connects to Port 4 of the Fat Pipe Region of the AMC backplane connector. The implementation of PCIe conforms to the AMC.1 specification.

- PCI Express External Cable Interface

The MAMC-XLINK includes a 1 – lane PCI Express External Cable Interface. The PCI Express External Cable Interface connects to a special PCI Express External Cable connector. The implementation of PCI Express External Cable Interface conforms to the PCI Express External Cabling Specification, Rev. 1.0.

- IPMI Controller

The MAMC-XLINK implements an IPMB interface which conforms to the AMC.0 specification. The IPMI firmware complies to the IPMI – Intelligent Platform Management Interface Specification, v1.5., Revision 1.1.

- Re-Driver Circuitry

The MAMC-XLINK includes Re-Driver circuitry, in order to guarantee PCIe signal quality at the receiver portion of the PCI Express External Cable Interface.

- Clock Selection

The MAMC-XLINK offers the choice to select between a local PCIe clock and the backplane clock FCLKA, which is defined in the AMC.0 specification.

## Board Specification

MAMC-XLINK Features

| AMC-Module | standard Advanced Mezzanine Card, single width, full height |
| --- | --- |
| Front-I/O | 1-lane PCI Express External Cable Connector |
| Firmware | IPMI firmware |
| Power consumption | 12V 0.2A max. Payload Power 3.3V 0.1A max. Management Power |
| Environmental conditions | Temperature (operating): Temperature (storage): Humidity: | 0°C to +70°C with forced cooling -40°C to +85°C 10 % to 90 % rh noncondensing |
| Standards compliance | PICMG AMC.0 Rev. 2.0 PICMG AMC.1 Rev. 1.0 PICMG µTCA.0 Rev. 1.0 PCI Express Base Specification Rev. 1.1 PCI Express External Cabling Specification, Rev. 1.0 IPMI Specification v2.0 Rev. 1.0 |

# Installation

## Safety Note

To ensure proper functioning of the MAMC-XLINK take the following precautions before handling the board.

CAUTION

Electrostatic discharge and incorrect board installation and removal can damage circuits or shorten their life.

- Before installing or removing the MAMC-XLINK read this installation section

- Before installing or removing the MAMC-XLINK, read the Installation Guide and the User’s Manual of the carrier board used, or of the uTCA system the board will be plugged into.

- Before installing or removing the MAMC-XLINK on a carrier board or in a rack:
- Check all installed boards and modules for steps that you have to take

before turning on or off the power.
- Take those steps.
- Finally turn on or off the power if necessary.

- Make sure the part to be installed / removed is hot swap capable, if you don’t switch off the power.

- Before touching integrated circuits take all precautions required for handling electrostatic devices.

- Ensure that the MAMC-XLINK is connected to the carrier board or to the uTCA backplane with the connector completely inserted.

- When operating the board in areas of strong electromagnetic radiation ensure that the module
- is bolted to the front panel or rack
- and shielded by a screened enclosure

## Installation Prerequisites and Requirements

IMPORTANT

Before powering up

- check this section for installation prerequisites and requirements

### Requirements

The installation requires only

- an ATCA carrier board, or a µTCA backplane for connecting the MAMC-XLINK, with a PCI Express lane connected to Port 4

- power supply

- cooling devices

### Power supply

The power supply for the MAMC-XLINK must meet the following specifications:

- +12V  0.2A  Payload Power

- +3.3V 0.1A  Management Power

### Automatic Power Up

In the following situations the MAMC-XLINK will automatically be reset and proceed with a normal power up.

Voltage sensors

The voltage sensor generates a reset

- when +12V voltage level drops below 10V (payload power)

- when +3.3V voltage level drops below 3.08V (management power)

or when the carrier board / backplane signals AMC Disable.

### Thermal Considerations

The MAMC-XLINK can be operated in a temperature range of 0°C to +70°C if the air velocity does not fall below 1 m/s.

## Statement on Environmental Protection

### Compliance to RoHS Directive

Directive 2002/95/EC of the European Commission on the "Restriction of the use of certain Hazardous Substances in Electrical and Electronic Equipment" (RoHS) states that all electrical and electronic equipment being put on the European market after June 30th, 2006 may contain lead, mercury, hexavalent chromium, polybrominated biphenyls (PBB) and polybrominated diphenyl ethers (PBDE) and cadmium in maximum concentration values of 0.1% respective 0.01% by weight in homogenous materials only.

As these hazardous substances are currently used with semiconductors, plastics (i.e. semiconductor packages, connectors) and soldering tin, any hardware product is affected by the RoHS directive if it does not belong to one of the groups of products exempted from the RoHS directive.

Although many of the Meikon / N.A.T. hardware products are exempt from the RoHS directive it is the policy of Meikon / N.A.T. to produce compliant products wherever possible. Since January 31st, 2005 Meikon / N.A.T. has stipulated RoHS compliant components from its suppliers. RoHs compliance is also mandatory in the production process.

### Compliance to WEEE Directive

Directive 2002/95/EC of the European Commission on "Waste  Electrical and Electronic Equipment" (WEEE) mandates that manufacturers of electrical and electronic equipment which is put onto the European market have to contribute to the reuse, recycling and other forms of recovery of such waste. This directive makes reference to the Directive 2002/95/EC of the European Commission on the "Restriction of the use of certain Hazardous Substances in Electrical and Electronic Equipment" (RoHS).

Although  the main focus is on household use, the directive also affects business-to-business relationships. The directive is quite restrictive on how household waste has to be handled by the supplier/manufacturer; however, it allows a greater flexibility in business-to-business relationships. This is due to the fact that industrial electrical and electronic products are commonly integrated into larger and more complex environments or systems that cannot easily be dismantled when it comes to their disposal at the end of their life cycle.

As Meikon / N.A.T. products are sold solely to industrial customers, at the time of purchase the customer agrees to take the responsibility for a WEEE compliant disposal of the used Meikon / N.A.T. product. All Meikon / N.A.T. products are marked according to the directive with a crossed out bin to indicate that these products within the European Community must not be disposed with ordinary waste.

If you have any questions on the policy of Meikon / N.A.T. regarding the Directive 2002/95/EC of the European Commission on the "Restriction of the use of certain Hazardous Substances in Electrical and Electronic Equipment" (RoHS) or the Directive 2002/95/EC of the European Commission on "Waste  Electrical and Electronic Equipment" (WEEE) please contact Meikon / N.A.T. by phone or e-mail.

### Compliance to CE Directive

Compliance to the CE directive is declared. A ‘CE’ sign can be found on the PCB.

## Location Overview

Figure 3 "Location diagram of the MAMC-XLINK" shows the position of major components. Some of the components may not be populated depending on the board version..

Location Diagram of the MAMC-XLINK

# Functional Blocks

The MAMC-XLINK can be divided into a number of functional blocks, which are described in the following paragraphs.

## Re-Driver Circuitry

The MAMC-XLINK includes a Re-Driver circuitry, in order to guarantee PCIe signal quality at the receiver portion of the PCI Express External Cable Interface. There are different cables with different lengths on the market, which comply to the PCI Express External Cable Interface Specification. Although the specification does not specify   individual cable lengths, transmission characteristics require that the cable length should not exceed 7m. The Pericom PI2EQX4402D Re-Driver device installed on the MAMC-XLINK allows the user to adapt transmission charateristics to different cable lengths. As cable types and lengths will differ, it is not possible to give specific settings for the re-driver under all conditions. The user may need to adjust the settings if the default settings do not result in a satisfactory performance. With the MAMC-XLINK this can be done either in Software (by means of  programming the IPMI controller appropriately), or by switch settings. Please refer to chapters 5.6, 5.7, and 6.3 for a more detailed explanation. The PI2EQX4402D Re-Driver device implements four unidirectional ports, two of which are used on the MAMC-XLINK. Port A is used to drive the PCIe line from the AMC backplane to the PCI Express Cable Interface connector, Port C is used to drive the PCIe line from the PCI Express Cable Interface connector to the AMC backplane. Ports B and D are permanently disabled.

## IPMI Controller

The AVR ATmega645 microcontroller used to implement IPMI functionality integrates an SPI Programming Interface, an I2C interface, analogue inputs, and interrupt capabilities on some port pins. IPMI firmware makes use of some of these features. Please refer to chapters 4.2 and 6   for a more detailed explanation.

## IPMB Interface

The MAMC-XLINK implements an IPMB interface consisting of an AVR ATmega645 microcontroller and a temperature sensor. The IPMB controller also manages the hot swap functionality and the geographical address as requested by the AMC.0 specification.

## AMC Clock Interface

AMC backplane clock port FCLKA (Clock 3) is connected to a clock selector, in order to be used as a reference clock for PCI Express. FCLKA is only received. FCLKA is routed to a multiplexer, which allows programming the clock source of the PCI Express External Cable Interface to be either FCLKA, or an internal differential 100 MHz reference clock.

The MAMC-XLINK is always clock master of the PCI Express External Cable Interface, i.e. the clock is transmitted to the cable interface, but not received from there.

## Cable Interface Control Signals

The PCI Express External Cable Interface implemented on the MAMC-XLINK supports the following Cable Interface control signals:

CPERST#, CPRSNT#, CWAKE#, CPWRON

For definition, usage, sensing, and programming of these control signals please refer to chapter 6.3 and to the PCI Express External Cable Interface Specification.

# Hardware Description

## AMC Port Definition

AMC Port Definition

|  | Port No. | AMC Port Mapping Strategy | Ports used as |
| --- | --- | --- | --- |
| Basic Connector | CLK1 | Clocks | unassigned |
|  | CLK2 |  | unassigned |
|  | CLK3 |  | Reference Clock 3 (FCLKA, PCI Express Clock) |
|  | 0 | Common Options Region | unassigned |
|  | 1 |  | unassigned |
|  | 2 |  | unassigned |
|  | 3 |  | unassigned |
|  | 4 | Fat Pipes | PCI Express Lane 0 |
|  | 5 |  | unassigned |
|  | 6 |  | unassigned |
|  | 7 |  | unassigned |
| Extended Connector | 8 | Region | unassigned |
|  | 9 |  | unassigned |
|  | 10 |  | unassigned |
|  | 11 |  | unassigned |
|  | 12 | Extended Options Region | unassigned |
|  | 13 |  | unassigned |
|  | 14 |  | unassigned |
|  | 15 |  | unassigned |
|  | CLK4/5 |  | unassigned |
|  | 17 |  | unassigned |
|  | 18 |  | unassigned |
|  | 19 |  | unassigned |
|  | 20 |  | unassigned |

For proper operation, the MAMC-XLINK requires a PCI Express Lane to be connected to Port 4 of the AMC connector.

## Definition of ATmega645 Port Pins

ATmega645 port pins are used to communicate with the PCI Express External Cabling Interface and to set up some Re-Driver configuration as follows:

ATmega645 Port Pin Usage (Port A)

| Signal Function | PowerQUICC III Port A Pin | Description |
| --- | --- | --- |
| /HS_SW | PA7 | Hot Swap Switch |
| PWRGD | PA6 | Power Good Indicator |
| /IALERT | PA5 | Power Good Indicator |
| GA_PALLUP | PA4 | driver for Geographical Address sensing |
| GA2 | PA3 | Geographical Address 2 |
| GA1 | PA2 | Geographical Address 1 |
| GA0 | PA1 | Geographical Address 0 |
| /AMC_ENABLE | PA0 | Enable AMC module |

ATmega645 Port Pin Usage (Port B)

| Signal Function | PowerQUICC III Port B Pin | Description |
| --- | --- | --- |
| /CPRSNT | PB7 | PCIe Cable Interface present indicator |
| not used | PB6 | pin is unconnected |
| /PWRON | PB5 | Power On PCIe Cable Interface control pin |
| /PERST | PB4 | PCIe Reset Output |
| MISO | PB3 | SPI programming interface |
| MOSI | PB2 | SPI programming interface |
| SCLK | PB1 | SPI programming interface |
| not used | PB0 | pin is unconnected |

ATmega645 Port Pin Usage (Port C)

| Signal Function | PowerQUICC III Port C Pin | Description |
| --- | --- | --- |
| EN_A | PC7 | enable Port A programmability |
| SEL_A6 | PC6 | SEL6 Re-Driver Port A |
| SEL_A5 | PC5 | SEL5 Re-Driver Port A |
| SEL_A4 | PC4 | SEL4 Re-Driver Port A |
| SEL_A3 | PC3 | SEL3 Re-Driver Port A |
| SEL_A2 | PC2 | SEL2 Re-Driver Port A |
| SEL_A1 | PC1 | SEL1 Re-Driver Port A |
| SEL_A0 | PC0 | SEL0 Re-Driver Port A |

ATmega645 Port Pin Usage (Port D)

| Signal Function | PowerQUICC III Port D Pin | Description |
| --- | --- | --- |
| EN_C | PD7 | enable Port C programmability |
| SEL_C6 | PD6 | SEL6 Re-Driver Port C |
| SEL_C5 | PD5 | SEL5 Re-Driver Port C |
| SEL_C4 | PD4 | SEL4 Re-Driver Port C |
| SEL_C3 | PD3 | SEL3 Re-Driver Port C |
| SEL_C2 | PD2 | SEL2 Re-Driver Port C |
| SEL_C1 | PD1 | SEL1 Re-Driver Port C |
| SEL_C0 | PD0 | SEL0 Re-Driver Port C |

ATmega645 Port Pin Usage (Port E)

| Signal Function | PowerQUICC III Port E Pin | Description |
| --- | --- | --- |
| PCIE_CLKSEL | PE7 | select the PCIe clock |
| CWAKE# | PE6 | CWAKE# signal from Cable Interface |
| SDA | PE5 | I2C bus to AMC backplane, IPMB |
| SCL | PE4 | I2C bus to AMC backplane, IPMB |
| /RED_LED | PE3 | controls the red LED on the front panel |
| /BLUE_LED | PE2 | controls the blue LED on the front panel |
| SDA_INT | PE1 | internal I2C bus to Temperature Sensor |
| SCL_INT | PE0 | internal I2C bus to Temperature Sensor |

ATmega645 Port Pin Usage (Port F)

| Signal Function | PowerQUICC III Port F Pin | Description |
| --- | --- | --- |
| not used | PF7 | pin is unconnected |
| not used | PF6 | pin is unconnected |
| not used | PF5 | pin is unconnected |
| not used | PF4 | pin is unconnected |
| not used | PF3 | pin is unconnected |
| not used | PF2 | pin is unconnected |
| 1.8V_SENSE | PF1 | analogue/digital converter sense input for +1.8V supply voltage |
| 3.3V_SENSE | PF0 | analogue/digital converter sense input for +3.3V supply voltage |

ATmega645 Port Pin Usage (Port G)

| Signal Function | PowerQUICC III Port G Pin | Description |
| --- | --- | --- |
| /RST_IPMI | PG5 | RESET input to IPMI controller |
|  | PG4 | controls the yellow LED on the front panel |
|  | PG3 | controls the green LED on the front panel |
| not used | PG2 | pin is unconnected |
| LED4 | PG1 | controls LED 4 on the front panel LED block |
| LED3 | PG0 | controls LED 3 on the front panel LED block |

## Front Panel LEDs

The front panel LEDs are divided into 2 groups:

  - the LEDs specified by the AMC.0 standard

  - a block of 4 LEDs above the PCI Express External Cable connector

### AMC Standard LEDs

The AMC standard defines 4 LEDs, located on the lower / right side of the front panel, two of which are mandatory, and two of which are optional. The MAMC-XLINK supports all of these LEDs.

There are two general status LEDs, a blue LED, and a red LED. These LEDs are controlled by IPMI firmware. The other two LEDs, a green LED and a yellow LED, are optional. They are supplied, but their use depends on user’s software.

### 4 LED Block

There is a 4 LED block located above the PCI Express External Cable connector. LEDs 1 and 2 of this block show the link status of the Re-Driver PCIe lines. LEDs 3 and 4 are programmable by the user.

All programmable LEDs are controlled by the ATmega645 microcontroller. For further information on how to program these LEDs please refer to the ATmega325/3250/645/6450/V Product Data Book, or turn to Meikon / N.A.T. for further assistance.

# Connectors and Switches

## Connector Overview

Connectors of the MAMC-XLINK

Please refer to the following tables to look up the connector pin assignment of the MAMC-XLINK.

## AMC Connector CON1

AMC Connector CON1

| Pin No. | AMC-Signal | AMC-Signal | Pin No. |
| --- | --- | --- | --- |
| 1 | GND | GND | 170 |
| 2 | PWR | TDI | 169 |
| 3 | /PS1 | TDO | 168 |
| 4 | PWR_IPMB | /TRST | 167 |
| 5 | GA0 | TMS | 166 |
| 6 | RESVD | TCK | 165 |
| 7 | GND | GND | 164 |
| 8 | RESVD | NC | 163 |
| 9 | PWR | NC | 162 |
| 10 | GND | GND | 161 |
| 11 | XLINK1_P | NC | 160 |
| 12 | XLINK1_N | NC | 159 |
| 13 | GND | GND | 158 |
| 14 | RLINK1_P | NC | 157 |
| 15 | RLINK1_N | NC | 156 |
| 16 | GND | GND | 155 |
| 17 | GA1 | NC | 154 |
| 18 | PWR | NC | 153 |
| 19 | GND | GND | 152 |
| 20 | NC | NC | 151 |
| 21 | NC | NC | 150 |
| 22 | GND | GND | 149 |
| 23 | NC | NC | 148 |
| 24 | NC | NC | 147 |
| 25 | GND | GND | 146 |
| 26 | GA2 | NC | 145 |
| 27 | PWR | NC | 144 |
| 28 | GND | GND | 143 |
| 29 | NC | NC | 142 |
| 30 | NC | NC | 141 |
| 31 | GND | GND | 140 |
| 32 | NC | NC | 139 |
| 33 | NC | NC | 138 |
| 34 | GND | GND | 137 |
| 35 | NC | NC | 136 |
| 36 | NC | NC | 135 |
| 37 | GND | GND | 134 |

| Pin No. | AMC-Signal | AMC-Signal | Pin No. |
| --- | --- | --- | --- |
| 38 | NC | NC | 133 |
| 39 | NC | NC | 132 |
| 40 | GND | GND | 131 |
| 41 | /ENABLE | NC | 130 |
| 42 | PWR | NC | 129 |
| 43 | GND | GND | 128 |
| 44 | PET0_P_P4 | NC | 127 |
| 45 | PET0_N_P4 | NC | 126 |
| 46 | GND | GND | 125 |
| 47 | PER0_P_P4 | NC | 124 |
| 48 | PER0_N_P4 | NC | 123 |
| 49 | GND | GND | 122 |
| 50 | NC | NC | 121 |
| 51 | NC | NC | 120 |
| 52 | GND | GND | 119 |
| 53 | NC | NC | 118 |
| 54 | NC | NC | 117 |
| 55 | GND | GND | 116 |
| 56 | IPMB_SCL | NC | 115 |
| 57 | PWR | NC | 114 |
| 58 | GND | GND | 113 |
| 59 | NC | NC | 112 |
| 60 | NC | NC | 111 |
| 61 | GND | GND | 110 |
| 62 | NC | NC | 109 |
| 63 | NC | NC | 108 |
| 64 | GND | GND | 107 |
| 65 | NC | NC | 106 |
| 66 | NC | NC | 105 |
| 67 | GND | GND | 104 |
| 68 | NC | NC | 103 |
| 69 | NC | NC | 102 |
| 70 | GND | GND | 101 |
| 71 | IPMB_SDA | NC | 100 |
| 72 | PWR | NC | 99 |
| 73 | GND | GND | 98 |
| 74 | NC | NC | 97 |
| 75 | NC | NC | 96 |
| 76 | GND | GND | 95 |
| 77 | NC | NC | 94 |
| 78 | NC | NC | 93 |

| Pin No. | AMC-Signal | AMC-Signal | Pin No. |
| --- | --- | --- | --- |
| 79 | GND | GND | 92 |
| 80 | FCLKA_P | NC | 91 |
| 81 | FCLKA_N | NC | 90 |
| 82 | GND | GND | 89 |
| 83 | /PS0 | NC | 88 |
| 84 | PWR | NC | 87 |
| 85 | GND | GND | 86 |

## Front Panel Connector CON2

Table 12:  shows the pin assignment of PCI Express External Cable Interface connector.

Pin Assignment of the Front Panel Connector CON2

| Pin No. | Signal | Signal | Pin No. |
| --- | --- | --- | --- |
| A1 | CPER0_N | GND | B1 |
| A2 | CPER0_P | not connected | B2 |
| A3 | not connected | CWAKE# | B3 |
| A4 | SB_RTN | CPRSNT# | B4 |
| A5 | CFRECLK_N | GND | B5 |
| A6 | CFRECLK_P | not connected | B6 |
| A7 | not connected | CPWRON | B7 |
| A8 | CPERST# | CPET0_N | B8 |
| A9 | GND | CPET0_P | B9 |

## AVR Programming Port Connector JP1

Connector JP1 connects the SPI- or programming port of the AVR ATmega645 microcontroller.

ATmega645 Programming Port JP1

| Pin No. | Signal | Signal | Pin No. |
| --- | --- | --- | --- |
| 1 | MISO | +3.3V | 2 |
| 3 | SCLK | MOSI | 4 |
| 5 | /RST_IPMI | GND | 6 |

## Hot Swap Switch SW1

Switch SW1 is used to support hot swapping of the module. It conforms to PICMG AMC.0.

## DIL Switch SW2

The PI2EQX4402D Re-Driver device implements four unidirectional ports, two of which are used on the MAMC-XLINK. DIL switch SW2 is used to set the line transmission characteristics of Re-Driver A, which drives the PCIe line from the AMC backplane to the PCI Express Cable Interface connector.

Switch Assignment of DIL Switch SW2

| Switch No. | Signal | Default Setting |
| --- | --- | --- |
| Pos. 1 | SEL_A0 | on |
| Pos. 2 | SEL_A1 | on |
| Pos. 3 | SEL_A2 | on |
| Pos. 4 | SEL_A3 | on |
| Pos. 5 | SEL_A4 | on |
| Pos. 6 | SEL_A5 | on |
| Pos. 7 | SEL_A6 | on |
| Pos. 8 | not used | on |

## DIL Switch SW3

The PI2EQX4402D Re-Driver device implements four unidirectional ports, two of which are used on the MAMC-XLINK. DIL switch SW3 is used to set the line transmission characteristics of Re-Driver C, which drives the PCIe line from the PCI Express Cable Interface connector to the AMC backplane.

Switch Assignment of DIL Switch SW2

| Switch No. | Signal | Default Setting |
| --- | --- | --- |
| Pos. 1 | SEL_C0 | on |
| Pos. 2 | SEL_C1 | on |
| Pos. 3 | SEL_C2 | on |
| Pos. 4 | SEL_C3 | on |
| Pos. 5 | SEL_C4 | on |
| Pos. 6 | SEL_C5 | on |
| Pos. 7 | SEL_C6 | on |
| Pos. 8 | not used | on |

The default settings for both switches SW2 and SW3 have been successfully tested with various cable lengths and should work without change with most user applications.

# MAMC-XLINK Programming Notes

## AMC Control Signals

The AMC control signals /AMC_ENABLE, GA2 – 0, GA_PULLUP are sensed or set by IPMI firmware. The same applies for control of the AMC LEDs and handling of hot swap events. For further information please turn to N.A.T. GmbH.

## Selecting the PCIe Clock Source

The PCIe clock source can either be the FCLKA clock taken from the AMC backplane, or a local 100 MHz oscillator. ATmega645 microcontroller’s port pin PE7 selects the clock source. When PE7 is set “low”, FCLKA is the clock source. When PE7 is set “high”, the internal oscillator sources the PCI Express External Cable Interface.

## PCI Express External Cable Interface Control Signals

The PCI Express External Cable Interface control signals CPERST#, CPRSNT#, CWAKE#, CPWRON are controlled by firmware.

CPERST# is sent downstream the PCI Express External Cable Interface by the MAMC-XLINK either when programmed by port pin PB4 of the ATmega645 microcontroller, or as long as no module is sensed downstream, i.e. CPRSNT# is “high”.

By driving CPRSNT# “low” the downstream system indicates to the upstream system that it has been powered up and is functional. This signal is sensed by ATmega645 microcontroller firmware.

By driving CWAKE# “low” the downstream system indicates to the upstream system that it shall power up. This function is optional and not implemented.

CPWRON# is sent downstream the PCI Express External Cable Interface by the MAMC-XLINK when programmed by port pin PB5 of the ATmega645 microcontroller, in order to tell the downstream system that it shall power up. This function is optional, and its implementation depends on the hardware of the downstream system. MAMC-XLINK firmware doesn’t use this feature.

For further information on how to handle these control signals please refer to the PCI Express External Cable Interface Specification and contact N.A.T. GmbH.

## Programming the Re-Driver Device Strapping Pins

The Pericom PI2EQX4402D Re-Driver device installed on the MAMC-XLINK allows the user to adapt transmission charateristics to different cable lengths. This strapping may be done either by software or by setting the 2 DIL switches SW2 and SW3. By default, setting the strapping pins by software is disabled.

When the DIL switches are used for strapping, ATmega645 microcontroller’s port pins PC7 and PD7 have to be set to “high”, which can either be done by programming these port pins appropraitely, or by not programming them at all (default). In this case a pull-up resistor pulls the enable signals high.

### Re-Driver Strapping Pins Description

The Re-Driver Strapping Pins set the transmission line driver characteristics. Their influence on the transmission line driver characteristics is as follows:

Re-Driver Strapping Pins SEL0 – 2, Equalizer Selection

| SEL0 | SEL1 | SEL2 | Compliance Channel |
| --- | --- | --- | --- |
| 0 | 0 | 0 | No Equalisation |
| 0 | 0 | 1 | [0:1.5dB] @ 1.25 GHz |
| 0 | 1 | 0 | [0:2.5dB] @ 1.25 GHz |
| 0 | 1 | 1 | [0:3.5dB] @ 1.25 GHz |
| 1 | 0 | 0 | [0:4.5dB] @ 1.25 GHz |
| 1 | 0 | 1 | [0:5.5dB] @ 1.25 GHz |
| 1 | 1 | 0 | [0:6.5dB] @ 1.25 GHz |
| 1 | 1 | 1 | [0:7.5dB] @ 1.25 GHz |

Re-Driver Strapping Pins SEL3 – 4, Output Swing Control

| SEL3 | SEL4 | Swing |
| --- | --- | --- |
| 0 | 0 | 1 x |
| 0 | 0 | 0.8 x |
| 0 | 1 | 1.2 x |
| 0 | 1 | 1.4 x |

Re-Driver Strapping Pins SEL5 – 6, Output De-emphasis Adjustment

| SEL5 | SEL6 | De-emphasis |
| --- | --- | --- |
| 0 | 0 | 0 dB |
| 0 | 0 | -2.5 dB |
| 0 | 1 | -3.5 dB |
| 0 | 1 | -4.5 dB |

If the setting of the transmission line driver characteristics shall be done by software, please turn to Meikon / N.A.T. GmbH for further assistance.

## Setup of the Serial Interfaces

### I2C Interfaces

There are two I2C interfaces connected to the ATmega645 microcontroller’s port pins.

The 1st one connects port pins PE0 (Clk) and PE1 (Data) to a LM75 temperature sensor. The address of this sensor is 0.

The 2nd I2C interface is connected to port pins PE4 (Clk) and PE5 (Data). This I2C interface is routed to the IPMB interface of the AMC backplane.

IPMI firmware programs these two interfaces.

### SPI Interface

The SPI interface is connected to port pins PB3 (SPIMISO), PB2 (SPIMOSI), and PB1 (SCLK). It is used for in-system-programming of the AVR ATmega645 microcontroller.

# Known Bugs / Restrictions

  - Re-Driver link sense circuitry not functionable, link status not diplayed correctly on LEDs 1 and 2

Appendix A: Reference Documentation

[1]	Pericom, PI2EQX4402D 2.5Gbps x2 Lane Serial PCI Express Repeater / Equalizer

with Signal Detect feature, 11/06

[2]	Atmel, ATmega325/3250/645/6450/V Product Data, Rev. 2570L, 08/07

[3]	PCI Local Bus Specification, Revision 3.0, February 3, 2004

[4]	PCI Express Base Specification, Revision 2.0, December 20, 2006

[5]	IPMI – Intelligent Platform Management Interface Specification, v1.5. Revision 1.1,

February 20, 2002

[6]	AdvancedTCA Base Specification (PICMG 3.0 R1.0), December 30, 2002,

and as amended by ECN 3.0-1.0-001

[7]	PCI Express External Cabling Specification, Revision 1.0, January 4, 2007

Appendix B: Document’s History

| Revision | Date | Description | Author |
| --- | --- | --- | --- |
| 1.0 | 01/19/2009 | initial revision | ga |

# Text boxes

Note:

The release of the Hardware Manual is related to a particular HW board revision given in the document title. For earlier hardware revisions please contact Meikon or N.A.T. for the relevant Hardware Manual release.