Impressora térmica Bluetek

VS-TP5802US

Manual de instruções

Instruções

Informações iniciais:

Bluetek impressora térmica conta com uma impressão térmica com alta velocidade, boa qualidade e tecnologia avançada.

Devido ao seu pequeno volume e de fácil operação e comparativa, que é amplamente utilizado em muitas áreas, tais como supermercado, restaurante, farmácia, rede de fast-food, hospital, banco, posto de gasolina e assim por diante.

Para operar sua impressora precisa e eficiente com uma vida mais longa para seus produtos, por favor leia atentamente este manual.

1. Cabeça térmica de impressão gera componente calor, por isso, não toque na cabeça de impressão e no componente próximo ao lado com a sua figura ao imprimir ou apenas terminar a impressão.

2. Não toque na superfície da cabeça de impressão no caso de destruí-lo.

3. A impressora deve ser colocada em um determinado lugar estável para evitar no lugar de vibrações.

4. Conecte o adaptador da impressora a uma tomada adequada, evite utilização de extensões

5. Não deve funcionar sem papel, ou ele vai danificar seriamente a cabeça de impressão.

6. Por favor, desligue a energia do adaptador, se você não utilizar por um longo período.

7. Os usuários estão proibidos de desmontar a impressora para consertar ou refazê-lo pessoalmente.

8. O adaptador só é permitido usar um especial.

9. A fim de certificar-se da qualidade de impressão e de longo tempo de vida, sugerimos usar o papel de impressão térmica recomendada ou com a mesma qualidade.

10. Quando você tirar a ficha, por favor, certifique-se de que a energia esteja desligada.

11. Quando a impressora está começando com equipamentos de fora, por favor ligue o equipamento do lado de fora, em seguida, a impressora, quando desligado, por favor, desligue a impressora, em seguida, o equipamento externo.

12. Mantenha o manual guardado, para utilizar como referencia.

Contents

Principais características 	4

Especificações Técnicas	4

Conteúdo da Embalagem	5

Formas de conexão 	5

Diretrizes para conexão	5

Ligar impressora	5

Botão e luz indicadora	5

Verificação automática impressora 	6

Operação de Exame automática	6

A função de Interface Serial	6

A conexão da interface serial	6

A função de conexão de interface paralela	7

Ordenação instrução de comando 	8

1. Principais características

● Baixo nível de ruído e alta velocidade de impressão

● alta qualidade do trabalho de impressão

● estrutura leve e super compacto, aparência atraente

● Aumentar as letras e ajustar a distância entre as letras

● Capaz de imprimir fotos em diferentes densidades.

● de baixa potência, baixo custo (sem necessidade de fita e cartucho)

● Compatível com ESC / POS ordem

2. Especificações Técnicas

● Térmica Sistema Ponto Linha

● Largura do papel: 57 milímetros

● Velocidade de impressão: 70 mm / s

● Função da cabeça de impressão: 384 pontos / linha

● Tempo de Vida: 50 km

Nota:  A cabeça de impressão tem a função de evitar superaquecimento.

A luz "Mode" irá ligar quando a temperatura da impressora fica alta e a impressora pára automaticamente a impressão. Uma vez que se trata de voltar à temperatura normal, a impressora continuar a imprimir novamente.

3. Conteúdo da Embalagem

Desembale a impressora e verifique o seu conteúdo para garantir que a impressora e todos os acessórios como mostrado abaixo estão incluídos.

| Impressora VS-TP5802US | 1 unidade |
| --- | --- |
| Fonte de energia | 1 unidade |
| Cabo | 1 unidade |
| Manual de instruções | 1 unidade |

4. Formas de conexão:

Certifique-se de que o equipamento de impressão e externo foi desligado, conecte o cabo de comunicação para a impressora e interface paralela com 25 pinos ou interface serial com 9 pinos para o equipamento externo.

Se a impressora que está ligada a uma gaveta de dinheiro, a especificação da gaveta de dinheiro devem respeitar o condutor gaveta de dinheiro.

5. Ligar impressora

Fonte de alimentação é controlada pelo interruptor ON / OFF.

6. Botão e luz indicadora

- FEED ------

- ONLINE Muda impressora on-line ou off-line

- MODE. Mostra o status atual.  ON - Impressora ligada, OFF - Impresora desligada.

7. Verificação automatica impressora

A impressora irá auto imprimir uma lista de verificação, incluindo texto se tudo estiver em situação normal.

8. Operação de Exame automática

Ligue a impressora à fonte de alimentação, mantenha pressionado o botão FEED e no mesmo tempo o botão ON, pressionando 5 segundos e depois solte a tecla, a impressora vai imprimir a lista exame automático

9. Função da impressora serial de interface

| Pin no. | Signal Name | Signal Resource | Description |
| --- | --- | --- | --- |
| 2 | TXD | Printer | When it adapts to XON/XOFF protocol, the printer send control code XON/XOFF to the host machine |
| 3 | RXD | Host | The printer gains data from the host |
| 4 | RTS | Printer | RTS indicates that it is in the state of printing. Low power means the printer is busy, failing to receive data, while high power means it is ready to print and able to receive data. |
| 7 | GND | ---- | Signal ground |
| 20 | DTR | printer | The same with signal RTS |

10. A de conexão da interface serial.

Serial interface connection of printer DB-25/Serial interface connection of host DB-9

11.  A função de conexão de interface paralela:

| Lead pin | Signal name | Signal source | Description |
| --- | --- | --- | --- |
| 1 | /STB | Host | Data strobe trigger pulses, it actives at low level |
| 2 3 4 5 6 7 8 9 | DATA0 DATA1 DATA2 DATA3 DATA4 DATA5 DATA6 DATA7 | host host host host host host host host | Those signals represent parallel date from the first message to the eighth. When the logic is "1" to "high" level, logic "0" to "low" level |
| 10 | ACK | Printer | The printer reacts to the signal, which indicates that the printer has received the prior date. |
| 11 | BUSY | printer | Signal of BUSY. When it is at high level for printer busy, unable to receive data. |
| 12 | PE | Printer | Signal of lacking paper for the printer |
| 13 | SLCT | Printer | Pull-through by resistance to high level |
| 15 | ERR | printer | Printer Error |
| 16 | INIT | host | Printer Initializing |
| 14, 17 | NC | ------ | Not connected |
| 18-25 | GND | ------ | Signal ground |

12. Ordenação instrução de comando

HT                                           Horizontal tab

[Format] ASCII：HT Hex：09 Decimal：9

[Description] ●Move from the current place to next skipping place ●If the next horizontal tab surpassed the final position, this command is not executed ●The position of horizontal tab is set by ESCD orders. ●The default tab position is standard ASCll characters in every 8 (12x24) characters in a cell jump.

LF                                           Print and feed

[Format] ASCII：LF Hex：0A Decimal：10

[Description] ● Print data in the buffer zone and feed the paper. ●When the buffer zone is empty, only forward a linen of the paper. ●This command puts the current position in the first line.

DLE EOT                      Current Transmission Status

[Format] ASCII： DLE EOT n Hex： 10 04 n Decimal： 16 4 n

[Range] 1≤n≤4 [Description] Temper designations:

|  |  | Value ON/OFF |
| --- | --- | --- |
| Digit | function | 1 | 0 |
| 0 | Mistake state | Error | Normal |
| 1 | Temperature state | High | Normal |
| 2 | Head up | Head up | Normal |
| 3 | Paper Exhaust | Paper exhaust | Normal |
| 4 | Online state | offline | Online |
| 5 | Un-definition |  |  |
| 6 | Un-definition |  |  |
| 7 | Un-definition |  |  |

ESC ！                                 Choose Printing Mode

| [Format] ASCII： ESC ！ n Hex： 1B 21 n Decimal ： 27 33 n |
| --- |
| [Range] 0≤n≤255 [Description] Printing mode according to the setting of N |
| Digit | Function | Value ON/OFF |
|  |  | 1 | 0 |
| 0 | Un-definition | —— | —— |
| 1,2 | Un-definition | —— | —— |
| 3 | Un-definition | —— | —— |
| 4 | Double-height | select | Cancel |
| 5 | Double-width | select | cancel |
| 6 | Un-definition | —— | —— |
| 7 | Un-definition | —— | —— |

ESC %                Enable / Disable User-defined Characters

[Format] ASCII： ESC % n Hex： 1B 25 n Decimal： 27 37 n

[Range] 0≤n≤255 [Description] Select or cancel user-defined characters When MSB of n is for 0, inner flash ROM instead of user-defined characters is used. When LSB of n is for 1, user-defined characters is used. [Default value] n=0

ESC &                    Definition of User-defined Characters

[Format] ASCII： ESC & s n m [a[p]s×a]m-n+1 Hex： 1B 26 s n m [a[p]s×a]m-n+1 Decimal： 27 38 s n m [a[p]s×a]m-n+1

[Range] s=3，32≤n≤m≤126，0≤a≤12，0≤p≤255。 [Description]`● s represents for vertical printing, s=3. ●n represents for the beginning of definition characters in ASCll code ●m represents for the end of definition characters in ASCll code ●a for the printing point in horizonal direction ●P for character of user-defined, every character with s×a bytes, total for m-n+1 ●user definition has been in effect until further defining or reset or shut down ●When ASCll characters(12×24 are chosen.

ESC *                                  Bitmap Mode Option

[Format] ASCII： ESC * m n1 n2 [d] k Hex： 1B 2A m n1 n2 [d] k Decimal： 27 42 m n1 n2 [d] k

[Range] m=0，1，32，33，0≤n1≤255，0≤n2≤1，0≤d≤255 [Description] ●Point for vertical direction: n1+256×n2； ●If the printing point is beyond one line, the surpass data will be processed as normal data. ●。D is bitmap data byte, 1 for printing, 0 for no printing.

Select the bitmap mode assigned by m, and bitmap is control by n1 and n2

| m | mode | Vertical | Lateral |
| --- | --- | --- | --- |
|  |  | Point | Resolution ratio | Resolution ratio | Max points |
| 0 | 8 single-density | 8 | 60 DPI | 101 DPI | 192 |
| 1 | 8 single-density | 8 | 60 DPI | 203 DPI | 384 |
| 32 | 24 single-density | 24 | 180 DPI | 101 DPI | 192 |
| 33 | 24double-density | 24 | 180 DPI | 203 DPI | 384 |

● When 8 single-density is selected,

|  |  | d3 |  |
| --- | --- | --- | --- |

When 24 single density is selected:

ESC 2                                    Default Row Height

[Format] ASCII： ESC 2 Hex： 1B 32 Decimal： 27 50

[Description] ●Select 1/6 inches(about 4.23mm) row height

ESC 3                                    Setting Row Height

[Format] ASCII： ESC 3 n Hex： 1B 33 n Decimal： 27 51 n

[Range] 0≤n≤255 [Description] ●Set row height to[n×vertical or lateral moving unit] inches

ESC ？                      Cancel User-definition Characters

[Format] ASCII： ESC ？ n Hex： 1B 3F n Decimal： 27 63 n

[Range] 32≤n≤127 [Description] Cancel user-definition characters； ●Cancel code n in the user-definition. After canceling, inner mule-ucs is adapted. ●If it is not contained in defined character, this command is ignored.

ESC @                                     Initiating Printer

[Format] ASCII： ESC @ Hex： 1B 40 Decimal： 27 64

[Description] ●Clear up the data in buffer zone ●Restore default ●Restore default characters in printing mode ●Delete user-definition characters

ESC J                             Printing and Feeding Paper

[Format] ASCII： ESC J n Hex： 1B 4A n Decimal： 27 74 n

[Range] 0≤n≤255 [Description] ●Print data in buffer area and feed paper[n×vertical or lateral moving unit] inch ●When finishing printing, the current position will be put on the top. ●The distance of feeding is not affected by the ESC2 or ESC3.

ESC SO              Setting Double-width Character in Printing

[Format] ASCII： ESC SO Hex： 1B 0E Decimal： 27 14

[Description] ●All will be printed with double-width after execute the order. ●This command can be with drew by ENTER or ESC DC4.

ESC DC4      Cancel Setting Double-width Character in Printing

[Format] ASCII： ESC DC4 Hex： 1B 14 Decimal： 27 20

[Description] ●After this command is executed, the character is restored to normal printing;

ESC d                       Print and Feed forward to N Rows

[Format] ASCII： ESC d n Hex： 1B 64 n Decimal： 27 100 n

[Range] 0≤n≤255 [Description] Print the data in buffer zone and feed paper n rows ●With execution of this command, its printing position is set on the top. ●This order will not affect the line-spacing set by ESC2 or ESC3

ESC p                       Control Pulse Generated Cashbox

[Format] ASCII： ESC p m t1 t2 Hex： 1B 70 m t1 t2 Decimal： 27 112 m t1 t2

[Range] 0≤t1≤255，（t2 and m invalid, anyone is available） [Description] Output t1×2ms, the cashbox will use pulse

GS *                               Download Bitmap Defined

[Format] ASCII： GS * n1 n2 d[k] Hex： 1D 2A n1 n2 d[k] Decimal： 29 42 n1 n2 d[k]

[Range] 1≤n1≤48，1≤n2≤3，0≤d≤255； [Description] Defined one download bitmap, the points will be specified by n1 and n2. ●Lateral direction points: n1×8 ●Vertical direction points: n2×8 ●If it is beyond x×y, the order is invalid. ● d: bitmap data. 1 for print, 0 for no. ●Turn off the printer or reset, the down bitmap is cleared. ●The relationship between printing data and download bitmap

GS /                                  Print Download Bitmap

[Format] ASCII： GS / m Hex: 1D 2F m Decimal： 29 47 m

[Range] 0≤m≤3，48≤m≤51 [Description] Print a download bitmap, printing mode is specified by m. M selection mode： M Mode Vertical DPI Lateral DPI 0，48 Normal 180 203 1，49 Double-width 180 101 2，50 Double-height 90 203 3，51 Double width and height 90 101 ●The command is ignored if download bitmap is not defined. ●If the download bitmap is beyond the printing area, the surpassed parts will not be printed. ●This order will print the bitmap in RAM, when the printer power is switched off or reset, the bitmap will be cleared off.

FS  ！                        Setting Chinese Character Mode

[Format] ASCII： FS ！ n Hex： 1C 21 n Decimal： 28 33 n

[Range] 0≤n≤255 [Description] ●The printing mode of setting Chinese character with n: Digit Function Value ON/OFF 1 0 0 Un-definition ─ ─ 1 Un-definition ─ ─ 2 Double width Double width No 3 Double width Double width No 4 Un-definition ─ ─ 5 Un-definition ─ ─ 6 Un-definition ─ ─ 7 Un-definition ─ ─

FS  2                       User-definition of Defined Chinese

[Format] ASCII： FS 2 c1 c2 d1…dk Hex： 1C 32 c1 c2 d1…dk Decimal： 28 50 c1 c2 d1…dk

[Range] c1，c2 stands for defined code for characters c1=F8H；A1H≤c2≤FEH；0≤d≤255；k=72。 [Description] Character defined by c1, c2 ● c1，c2 stands for code of user-defined Chinese, c1 for the first byte;c2 for the second. ● d。Stands for data. 1 for print and 0 for not. Relationship between user-defined Chinese and data.

D1=00H, D4=00H, D7=00H, D10=10H……

D2=00H, D5=C0H, D8=E0H, D11=71H……

D3=00H, D6=60H, D9=70H, D12=F0H……

FS  ？             Cancel Definition of User-defined Characters

[Format] ASCII： FS ? c1 c2 Hex： 1C 3F c1 c2 Decimal： 28 63 c1 c2

[Range] c1=FAH；A1H≤c2≤FEH。 [Description] Cancelled by c1, c2 assinged user-defined Chinese characters.

FS  SO          Setting the Double-width of Chinese Characters

[Format] ASCII： FS SO Hex： 1C 0E Decimal： 28 14

[Description] ●When the command is executed, all Chinese will be printed in double-width ●The command will be withdrew by ENTER or FS DC4

FS  DC4      Withdraw the Double-width of Chinese Characters

[Format] ASCII： FS DC4 Hex： 1C 14 Decimal： 28 20

[Description] ●With this order, all Chinese will be printed normally.

# Text boxes

Bluetek - Automação Comercial

Ltd

TXD 2

RXD 3

RTS 4

GND 7

2 TXD

3 RXD

8 CTS

5 GND

12 ppponi

LSB

d1

d2

d3

d6

d5

d4

d7

d34

d35

d36

24

MSB

Bitmap data

MSB

Bitmap data data

LSB

Printing data

d1

d3

d2

Print data

□ 1 point

d2

d1

Double-density

Single-density

Bitmap data

Print data

MSB

Bitmap data

LSB

d1

d2

d3

d9

d8

d7

d4

d5

d6

Print data

□ 1point

双密度

d1　d2　d3　d4　d5　d6　d7　d8　d9

Double-density

Single-density

打印数据

打印数据

打印数据

x×8point

y×8piont

LSB

MSB

dy+1

dy×2+1

dy×2

dx×y×8

d1

d2

dy

24

LSB

MSB

24点

d1

d2

d3

d6

d5

d4

d7

d70

d71

d72