Verizon West

Order LSOG 5 & 6

October 2004 Release Overview

This document contains material which is a proprietary property of and confidential to VERIZON.

Disclosure outside VERIZON is prohibited except by written permission, license agreement or other

confidentiality agreement.  Unauthorized reproduction or distribution of this document in any

form or by any electronic or mechanical means is a expressly prohibited.

Copyright @2002 by VERIZON.  All Rights Reserved Worldwide

# TABLE OF CONTENTS

- REVISION HISTORY	4

- system release notification

- C02-2816 Flow Thru for Coin and Coin LNP	5

- C03-0167 – Flow Thru to Automate UNE-P PAL and UNE-P Coin Orders	7

- C03-0462 Flow Through Auto Rejects and Edits Phase 5, Part 2	9

- C03-1912 TRO Network Modifications for UNE Loops and IDLC Solution	10

- C03-1239 T5 POTS Service to Line Splitting (UNE-P) and No Previous Service to Line Splitting (UNE-P) - West	12

- C03-1162 T5 Hunt Group Data at Account Level Phase 2	16

- C03-2050 WISE "Contact Us" URL Modifications	21

- E03-0044 Modify E05/6FLDH02098 to make TC PER Optional on EU Form	22

- E04-0001 Remove edits to make TC PER Optional for RS and DDPS forms	23

- E04-0002 Modify edits for correct TOA values for Res Accts outside IL & SC	24

- E04-0007 Modify REQTYP/ACT/LNA edits to match Form Level META Edits	25

- E04-0009 Modify E05/6FLDH09767 not to invoke for a PO Box Address	26

- E04-0010 Remove/modify edits that will never invoke	27

- E04-0011 Modify E05/6FLDH01252 to include ACT=T	28

- E04-0012 Modify E05/6FLDH03124 to include Line Split	29

- E04-0015 Modify error messages for E05/6FLDH01477, 4245, 6128 and E06FLDH06650	30

- E04-0020 Modify edits to allow Hunt Forms for PBX & DID/DOD	31

- C03-1165 Allow Centranet Orders when ACT=V and existing profile is not Centranet	32

C03-1811 Expand the number of characters in the NAME field for Order and CSI	34

REVISION HISTORY

| Revision Date | Description of Change |
| --- | --- |

##### C02-2816 Flow Thru for Coin and Coin LNP

# Type: 4

Description:  This change request will automate certain types of CLEC’s request for coin orders.

Details:  Coin order requests are submitted as REQTYP=EB, ACT=W, V, N, C (PIC/LPIC Changes), S, B, D and V, TOS 2nd Character=C.  The new process will automate these orders and 5 new SIGS edits will be established.

A new SIGS edit (E05/6FLDH01427) will verify that the coin account is one that can be resold.  The edit will verify that on coin request of ‘as is’ and ‘as specified’ that the service is not a Public or Semi Public coin line. The edit will be on the LSR form, Admin section, ACT field:

REQTYP=EB & MB

TOS 2nd Character=C

ACT=W or V

If the request is for Public or Semi Public coin line then the LSR will be rejected back.

A new SIGS edit (E05/6FLDH01439) will verify that the requested account is an existing resalable coin account.  The edit will verify that for ‘as is’ requests the existing account is a customer owned pay telephone line.  The edit will be on the LSR form, Admin section, ACT field:

REQTYP=EB & MB

TOS 2nd Character=C

ACT=W

If the existing account is not a customer owned pay telephone line then the LSR will be rejected back.

Business Rule Impacts:  LSR/Admin/ACT, RS/Svc Det/LNA, and RS/Svc Det/FEATURE.

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 | 6 | LSR | Admin | ACT | E05FLDH01427 | E06FLDH01427 | Service not resalable. |
| New | 5 | 6 | LSR | Admin | ACT | E05FLDH01439 | E06FLDH01439 | Service not resalable. |
| New | 5 | 6 | RS | Svc Det | LNA | E05FLDH04237 | E06FLDH04237 | If REQTYP=EB, position 2 of TOS=C then only one iteration of LNA is allowed. |
| New | 5 | 6 | RS | Svc Det | LNA | E05FLDH04238 | E06FLDH04238 | If REQTYP=EB, ACT=V and position 2 of TOS=C then LNA cannot = N,D. |
| New | 5 | 6 | RS | Svc Det | FEATURE | E05FLDH04239 | E06FLDH04239 | If REQTYP=EB, position 2 of TOS=C then FLEX ANI CODE must be present. |

##### C03-0167 – Flow Thru to Automate UNE-P PAL and UNE-P Coin Orders

# Type: 4

Description:  This change request will automate certain types of CLEC’s request for UNE-P coin orders.

Details:  UNE-P PAL and UNE-P Coin order request are submitted as REQTYP=MB, ACT=N, D, C (PIC/LPIC Changes), S, and B, TOS 2nd Character=C.  The new process will automate these orders and 4 new SIGS edits will be established.

A new SIGS edit (E05/6FLDH01427) will verify that the UNE-P coin account is one that can be resold.  The edit will verify that on the UNE-P coin request of ‘as is’ and ‘as specified’ that the service is not a UNE-P Public or Semi Public coin line.  The edit will be on the LSR form, Admin section, Act field:

REQTYP=EB & MB

TOS 2nd Character=C

ACT=W or V

If the request is for UNE-P Public or Semi Public coin line then the LSR will be rejected back.

Business Rule Impacts:  LSR/Admin/ACT, PS/Svc Det/LNA and PS/Svc Det/FEATURE.

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 |  | LSR | Admin | ACT | E05FLDH01427 | E06FLDH01427 | Service not resalable. |
| New | 5 |  | PS | Svc Det | LNA | E05FLDH05202 | E06FLDH05202 | If REQTYP=MB, position 2 of TOS=C then only one iteration of LNA is allowed. |
| New | 5 |  | PS | Svc Det | LNA | E05FLDH05203 | E06FLDH05203 | If REQTYP=MB, ACT=V and position 2 of TOS=C then LNA cannot=N,D. |
| New | 5 |  | PS | Svc Det | FEATURE | E05FLDH05189 | E06FLDH05189 | If REQTYP=MB, ACT=N,V and position 2 of TOS=C then FLEX ANI CODE must be present. |

##### C03-0462 Flow Through Auto Rejects and Edits Phase 5, Part 2

Type: 4

Description:  When CLECs submit LSRs with Classified Headings not found in Verizon’s list of valid headings, the orders will be rejected.

Details:  An existing edit has been changed and a new edit has been created so that CLECs will receive appropriate edits when an invalid classified heading has been submitted.

A new Standardized Manual Edit (E05/6FLDH99822) will validate correct Yellow Page Headings (YPHV).

REQTYP=AB, MB, EB

ACT=N, R

REQTYP=EB

ACT=T

REQTYP=CB

ACT=V

An existing Standardized Manual Edit (E05/6FLDH99831) will be modified to no longer invoke on REQTYP=EB/ACT=N requests, and will continue to invoke under the following conditions:

REQTYP=JB

ACT=R, N, V

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the Standardized Manual edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 | 6 | DL | Advertising Section | YPHV | E05FLDH99822 | E06FLDH99822 | Classified Heading Entered is Not Valid. |
| Change | 5 | 6 | DL | Advertising Section | YPHV | E05FLDH99831 | E06FLDH99831 | Classified Heading Entered is Not Valid. |

##### C03-1912 TRO Network Modifications for UNE Loops and IDLC Solution

Type: 2

Description:  Verizon West will perform Network Modifications on UNE Loop and UNE Platform orders when a no facilities condition is encountered.   Network Modifications will only be available to CLECs that have signed a Triennial Review Order Amendment to their existing Interconnection Agreement.

Details:

Verizon West has added two new SUP values.

6 = Engineering query request

7 = Engineering charges accepted

Once a RN60 “No Facilities” jeopardy is received the CLEC has the following two options:

1 = SUP 1 to cancel request

2 = SUP 6 to request Engineering query information for the Routine Network Modification – Must have signed Triennial Review Order Amendment on file.

Verizon shall provide the CLEC with a quote for any required Engineering and Construction once a SUP 6 is received in response to a “no facilities” jeopardy.  An Engineering Query charge will apply for this quote.  Verizon will then return appropriate alpha code(s) to indicate the network modifications required and an estimated construction interval to perform the work.  This information will be returned on the LR form in response to the SUP 6 LSR.

After the quote is provided, the CLEC may request a Firm Construction order by placing a SUP 7 on the LSR authorizing Verizon to perform the required network modifications.  The CLEC will incur the Construction Charges quoted AND an Engineering Work Order Charge.

If, after Construction work has begun, the order is cancelled by the CLEC, cancellation charges will apply as well as a pro-rated charge for the construction work that has been completed to date.

Business Rule Impacts:

New fields added to the LR (Local Response):

- NMR = Network Modifications Required - Used to indicate the network modifications needed to fulfill the request.

- ECI = Engineering and Construction Interval - Used to indicate the number of business days required to perform the modification.  This interval must be added to the standard due date interval for the product to establish the new Due Date of the order.

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | LSR/Admin | 025 | SUP | New valid entries 6 = Engineering Query Request 7 = Engineering Charges Accepted |
| Change | LR/Admin | 016 | RT | New valid entry K= Network modification required |
| Add | LR/Ckt Detail | 52b | NMR |  |
| Add | LR/Ckt Detail | 52c | ECI |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | LSR/Admin | 025 | SUP | New valid entries 6 = Engineering Query Request 7 = Engineering Charges Accepted |
| Change | LR/Admin | 016 | RT | New valid entry K= Network modification required |
| Add | LR/Ckt Detail | 45b | NMR |  |
| Add | LR/Ckt Detail | 45c | ECI |  |

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 | 6 | LSR | Admin | CC | E05FLDH01458 | E06FLDH01458 | Product not available, unable to process request. |
| Change | 5 | 6 | LSR | Admin | SUP | E05FLDH01047 | E06FLDH01047 | If populated, valid values: 1,2,3,4,5,6,7. |
| New | 5 | 6 | LSR | Admin | SUP | E05FLDH01455 | E06FLDH01455 | If SUP=7, a SUP=6 must exist for same CCNA PON combination. |
| New | 5 | 6 | LSR | Admin | SUP | E05FLDH01482 | E06FLDH01482 | If REQTYP not = AB, BB, MB then SUP cannot = 6,7. |
| New | 5 | 6 | LSR | Admin | AENG | E05FLDH01456 | E06FLDH01456 | Required if SUP=6. |
| New | 5 | 6 | LSR | Admin | SCA | E05FLDH01457 | E06FLDH01457 | Required if SUP=7. |

The following table depicts the Standardized Manual edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 | 6 | LSR | Admin | SUP | E05FLDH99832 | E06FLDH99832 | CONTACT ACCOUNT MANAGER – REQUIRES TIME & MATERIALS |

##### C03-1239 T5 POTS Service to Line Splitting (UNE-P) and No Previous Service to Line Splitting (UNE-P) - West

Type: 5

Description:  The purpose of this initiative is to allow CLECs to use a single Local Service Request (LSR) for the new install of Voice and DSL service (UNE-P Line Split) same Due Date. This would include POTS Service (Verizon voice/No Data) to Line Splitting (UNE-P CLEC/voice/CLEC Data) and No previous service to Line Splitting (UNE-P CLEC voice/CLEC data).

Details:  POTS to Line Splitting Migration Requests are submitted as REQTYP=MB, ACT=V, SLI=S, and 2nd position of TOS=P.

No Previous Service to Line Splitting Requests are submitted as REQTYP=MB, ACT=N, SLI=S, and 2nd position of TOS=P.

There will be two new fields added to the PS Form.

1.  SDP – Shared Data Provider - Indicates the status of the shared data provider.

There are two valid entries:  A = NO Current data exists and B = Current Data Provider does exist.

This field will be required when migrating to Line Splitting.

2. ISR – Installation Service Requested - Identifies that the customer is requesting a provider technician to assist the end user with installation and configuration of on-site equipment.   Valid Entry: A = Installation and configuration of on-site equipment only.  A premise visit can be requested only when no current data provider exists.

Scenario 1:  The new process to migrate to Line Splitting on one LSR and there is existing POTS service is:

REQTYP=MB

ACT=V

TOS = 2nd position of P

SDP=A (no current data provider exists)

Scenario 2:  The new process to migrate to Line Splitting on one LSR and there is NO existing service is:

REQTYP=MB

ACT=N

TOS = 2nd position of P

SDP=A (no current data provider exists)

Business Rule Impacts:

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Add | PS/Service Detail | 039a | SDP – Shared Data Provider Field Length: 1 Characteristics: Alpha Indicator: Verizon Specific Usage: Conditional | Valid Entries: A = No Current data provider exists. B = Current data provider does exist. |
| Add | PS/Service Detail | 039b | ISR – Installation Service Requested Field Length: 1 Characteristics: A Indicator: Verizon Specific Usage: Optional | Valid Entries: A = Installation and configuration of on-site equipment only |
| Change | PS/Service Detail | 041 | SHELF Usage: From: Optional To: Conditional |  |
| Change | PS/Service Detail | 042 | SLOT Usage: From: Optional To: Conditional |  |
| Change | PS/Service Detail | 046 | CFA – Connecting Facility Assignment Usage: From: Optional To: Conditional |  |
| Change | EU/Disconnect Information | 054a | DISC ECCKT – Disconnect ECCKT Usage: From: Optional To: Conditional |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Add | PS/Service Detail | 042a | SDP – Shared Data Provider Field Length: 1 Characteristics: Alpha Indicator: Verizon Specific Usage: Conditional | Valid Entries: A = No Current data provider exists. B = Current data provider does exist. |
| Add | PS/Service Detail | 042b | ISR – Installation Service Requested Field Length: 1 Characteristics: A Indicator: Verizon Specific Usage: Optional | Valid Entries: A = Installation and configuration of on-site equipment only |
| Change | PS/Service Detail | 044 | SHELF Usage: From: Optional To: Conditional |  |
| Change | PS/Service Detail | 045 | SLOT Usage: From: Optional To: Conditional |  |
| Change | PS/Service Detail | 050 | CFA – Connecting Facility Assignment Usage: From: Optional To: Conditional |  |
| Change | EU/Disconnect Information | 060 | DISC ECCKT – Disconnect ECCKT Usage: From: Optional To: Conditional |  |

Edit Impacts:  Edits E05/6FLDH01313 and E05/6FLDH01464 were moved from the D/TSENT to the LSP AUTH field.

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| New | 5 | 6 | LSR | Admin | ACTL | E05FLDH01487 | E06FLDH01487 | Required if REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and first iteration of PS SDP is populated. |
| New | 5 | 6 | LSR | Admin | SLI | E05FLDH01486 | E06FLDH01486 | If REQTYP=MB, ACT=V, position 2 of TOS=P and first iteration of PS SDP is populated then SLI cannot =C. |
| Change | 5 | 6 | LSR | Admin | NC | E05FLDH01317 | E06FLDH01317 | NC/NCI Line Share to Line Split mismatch. |
| New | 5 | 6 | LSR | Admin | NC | E05FLDH01489 | E06FLDH01489 | If REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and first iteration of PS SDP=A then a Line Split NC is required. |
| Change | 5 | 6 | LSR | Admin | LSP AUTH | E05FLDH01313 | E06FLDH01313 | Line Split Ordering agreement does not exist. |
| Change | 5 | 6 | LSR | Admin | LSP AUTH | E05FLDH01464 | E06FLDH01464 | Loop Share Ordering agreement does not exist. |
| New | 5 | 6 | EU | Disconnect Information | DISC ECCKT | E05FLDH02152 | E06FLDH02152 | Prohibited if REQTYP=MB, ACT=N,V, SLI=S and position 2 of TOS=P. |
| New | 5 | 6 | EU | Disconnect Information | DISC NBR | E05FLDH02153 | E06FLDH02153 | Prohibited if REQTYP=MB, ACT=N,V, SLI=S and position 2 of TOS=P. |
| Change | 5 | 6 | PS | Service Detail | LNA | E05FLDH05074 | E06FLDH05074 | If position 2 of LSR TOS or PS LTOS=P then LNA cannot =L. |
| New | 5 | 6 | PS | Service Detail | LNA | E05FLDH05209 | E06FLDH05209 | If REQTYP=MB, ACT=V and position 2 of TOS=P then LNA cannot =D. |
| Change | 5 | 6 | PS | Service Detail | TNS | E05FLDH05078 | E06FLDH05078 | If REQTYP=MB, ACT=V, SLI=S, position 2 of TOS=P and first iteration of SDP=B then Line Share must exist on account defined by first iteration of TNS. |
| Change | 5 | 6 | PS | Service Detail | TNS | E05FLDH05201 | E06FLDH05201 | If REQTYP=MB, ACT=N,V and position 2 of TOS=P then exactly one iteration of TNS must be present. |
| New | 5 | 6 | PS | Service Detail | TNS | E05FLDH05219 | E06FLDH05219 | If REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and first iteration of SDP=A then data provider cannot exist. |
| New | 5 | 6 | PS | Service Detail | TNS | E05FLDH05211 | E06FLDH05211 | If REQTYP=MB, ACT=V, and position 2 of TOS=P then POTS account defined by first iteration of TNS cannot be UNE-P. |
| New | 5 | 6 | PS | Service Detail | SHELF | E05FLDH05210 | E06FLDH05210 | Required if REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and SDP is populated. |
| New | 5 | 6 | PS | Service Detail | SLOT | E05FLDH05212 | E06FLDH05212 | Required if REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and SDP is populated. |
| New | 5 | 6 | PS | Service Detail | CFA | E05FLDH05214 | E06FLDH05214 | Required if REQTYP=MB, ACT=N,V, SLI=S, position 2 of TOS=P and SDP is populated. |
| New | 5 | 6 | PS | Service Detail | SDP | E05FLDH05213 | E06FLDH05213 | Required if REQTYP=MB, ACT=N,V, SLI=S and position 2 of TOS=P. |
| New | 5 | 6 | PS | Service Detail | SDP | E05FLDH05215 | E06FLDH05215 | If populated, valid values: A,B. |
| New | 5 | 6 | PS | Service Detail | SDP | E05FLDH05216 | E06FLDH05216 | If ISR is populated then SDP must =A. |
| New | 5 | 6 | PS | Service Detail | SDP | E05FLDH05217 | E06FLDH05217 | If REQTYP=MB, ACT=N, SLI=S and position 2 of TOS=P then SDP cannot =B. |
| New | 5 | 6 | PS | Service Detail | ISR | E05FLDH05218 | E06FLDH05218 | If populated, valid value: A. |

##### C03-1162 T5 Hunt Group Data at Account Level Phase 2

##### Type:  5

Description:  This Change Request will refine up-front edits to more efficiently match Hunting IOSCs with the appropriate Hunting Telephone Numbers.

Details:  The new process to re-associate existing lines or adding new lines to an existing Hunt

Group is:

HA=C

HID=(Match the Hunt Group ID provided on CSI)

HLA=D (To remove all existing lines in hunt)

HLA=N (To re-establish lines in hunt in the new sequence)

Accounts in Florida and Hawaii will no longer require a tracking IOSC (05151).  For these two states, adding the appropriate Line Rate IOSC that carries Hunting will satisfy the edits.

UNE-P accounts across the West Footprint will no longer require a tracking IOSC (69301).  Adding the appropriate UNE-P IOSC’s for Hunting will satisfy the edits.

The process for requesting new lines in hunt will not change.

The process for a telephone number change of an existing line in Hunt will not change.

Business Rule Impacts:

Verizon West will make the following fields Not Supported:

LSOG 5 – LSR/Hunt Group Identification/TLI – Telephone Line Identifier, LSR/Hunt Group Identification/TLP – Telephone Line Identifier Type and LR/Hunt Group/TLI – Telephone Line Identifier.

LSOG 6:  HGI/Hunt Group Identification/TLI – Telephone Line Identifier, HGI/Hunt Group Identification/TIP – Telephone Line Identifier Type and LR/Hunt Group/TLI – Telephone Line Identifier.

The TLI, TLP (LSOG 5), TLI, TIP (LSOG 6) fields are no longer needed as the Hunt Groups are identified via the HID field, the Pilot Number in Hunt will be identified by adding it as the first line in the Hunt Sequence (HTSEQ).

For multiple Hunt Groups, blank hunt fields in WISE will no longer be passed to Verizon.

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | LSR/Hunt Group Identification | 114 | TLP – Telephone Line Identifier Type Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |
| Change | LSR/Hunt Group Identification | 115 | TLI – Telephone Line Identifier Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |
| Change | LR/Hunt Group | 039 | TLI – Telephone Line Identifier Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | HGI/Hunt Group Identification | 011 | TIP – Telephone Line Identifier Type Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |
| Change | LSR/Hunt Group Identification | 012 | TLI – Telephone Line Identifier Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |
| Change | LR/Hunt Group | 039 | TLI – Telephone Line Identifier Field Level Indicator: FROM: TO: VERIZON DOES NOT SUPPORT THE USE OF THIS FIELD. USAGE: FROM: Conditional TO: Not Supported |  |

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Add | 5 |  | LSR | Hunt Detail | HLA | E05FLDH01441 |  | If REQTYP=EB, ACT=C,V, HLA=D without HLA=N for same HT, then for that HT, the corresponding RS TNS or OTN must have RS FEATURE= a Hunt IOSC with RS FA=D. |
| Add | 5 |  | LSR | Hunt Detail | HLA | E05FLDH01442 |  | If REQTYP=MB, ACT=C,V, HLA=D without HLA=N for same HT, then for that HT, the corresponding PS TNS or OTN must have PS FEATURE= a Hunt IOSC with PS FA=D. |
| Change | 5 |  | LSR | Hunt Detail | HT | E05FLDH01399 |  | If REQTYP=EB and HT is populated with 10 or 14 characters, HT must exist within RS OTN, RS TNS or RS TNS range. |
| Change | 5 |  | LSR | Hunt Detail | HT | E05FLDH01400 |  | If REQTYP=MB and HT is populated with 10 or 14 characters, HT must exist within PS OTN, PS TNS or PS TNS range. |
| Change | 5 |  | LSR | Hunt Detail | HT | E05FLDH01311 |  | If REQTYP=EB,MB, HA does not =C or HLA does not =N,D then HT must be unique and not repeated. |
| New | 5 |  | LSR | Hunt Detail | HT | E05FLDH01444 |  | If REQTYP=EB,MB, HA=C and HLA=N,D then HT cannot be repeated unless matching HT has opposite HLA value. |
| Remove | 5 |  | LSR | Hunt Detail | HT | E05FLDH01268 |  | If LSR TLI is populated then first HT must match LSR TLI. |
| Change | 5 |  | LSR | Hunt Detail | HTSEQ | E05FLDH01392 |  | If REQTYP=EB,MB, HA does not =C or HLA does not =N,D then HTSEQ cannot be repeated with same HID value. |
| Change | 5 |  | LSR | Hunt Detail | HTSEQ | E05FLDH01395 |  | Required if REQTYP=EB and associated RS FEATURE contains a Hunt Group IOSC. |
|  |  |  | LSR | Hunt Detail | HTSEQ | E05FLDH01396 |  | Required if REQTYP=MB and associated PS FEATURE contains a Hunt Group IOSC. |
| New | 5 |  | LSR | Hunt Detail | HTSEQ | E05FLDH01445 |  | If REQTYP=EB,MB, HA=C and HLA=N,D then HTSEQ,HID combination cannot be repeated unless matching combination has opposite HLA value. |
| New | 5 |  | LSR | Hunt Detail | HTSEQ | E05FLDH01485 |  | HTSEQ must be in ascending order. |
| Remove | 5 |  | LSR | Hunt Group ID | TIP | E05FLDH01223 |  | Required if HA is populated. |
| Remove | 5 |  | LSR | Hunt Group ID | TIP | E05FLDH01224 |  | Valid values: T,L. |
| Remove | 5 |  | LSR | Hunt Group ID | TLI | E05FLDH01225 |  | Required if TIP is populated. |
| New |  | 6 | HGI | Hunt Detail | HLA |  | E06FLDH05561 | If REQTYP=EB, ACT=C,V, HLA=D without HLA=N for same HTN, then for that HTN, the corresponding RS TNS or OTN must have RS FEATURE= a Hunt IOSC with RS FA=D. |
| New |  | 6 | HGI | Hunt Detail | HLA |  | E06FLDH05562 | If REQTYP=MB, ACT=C,V, HLA=D without HLA=N for same HTN, then for that HTN, the corresponding PS TNS or OTN must have PS FEATURE= a Hunt IOSC with PS FA=D. |
| Change |  | 6 | HGI | Hunt Detail | HTN |  | E06FLDH05549 | If REQTYP=EB and HTN is populated with 10 or 15 characters, HTN must exist within RS OTN, RS TNS or RS TNS range. |
| Change |  | 6 | HGI | Hunt Detail | HTN |  | E06FLDH05550 | If REQTYP=MB and HTN is populated with 10 or 15 characters, HTN must exist within PS OTN, PS TNS or PS TNS range. |
| Change |  | 6 | HGI | Hunt Detail | HTN |  | E06FLDH05531 | If REQTYP=EB,MB, HA does not =C or HLA does not =N,D then HTN must be unique and not repeated. |
| New |  | 6 | HGI | Hunt Detail | HTN |  | E06FLDH05559 | If REQTYP=EB,MB, HA=C and HLA=N,D then HTN cannot be repeated unless matching HTN has opposite HLA value. |
| Remove |  | 6 | HGI | Hunt Detail | HTN |  | E06FLDH05530 | If TLI is populated then first HTN must match TLI. |
| Change |  | 6 | HGI | Hunt Detail | HTSEQ |  | E06FLDH05542 | If REQTYP=EB,MB, HA does not =C or HLA does not =N,D then HTSEQ cannot be repeated with same HID value. |
| Change |  | 6 | HGI | Hunt Detail | HTSEQ |  | E06FLDH05545 | Required if REQTYP=EB and associated RS FEATURE contains a Hunt Group IOSC. |
| Change |  | 6 | HGI | Hunt Detail | HTSEQ |  | E06FLDH05546 | Required if REQTYP=MB and associated PS FEATURE contains a Hunt Group IOSC. |
| New |  | 6 | HGI | Hunt Detail | HTSEQ |  | E06FLDH05560 | If REQTYP=EB,MB, HA=C and HLA=N,D then HTSEQ,HID combination cannot be repeated unless matching combination has opposite HLA value. |
| New |  | 6 | HGI | Hunt Detail | HTSEQ |  | E06FLDH05564 | HTSEQ must be in ascending order. |
| Remove |  | 6 | HGI | Hunt Group ID | TIP |  | E06FLDH05515 | Required if HA is populated. |
| Remove |  | 6 | HGI | Hunt Group ID | TIP |  | E06FLDH05516 | Valid values: T,L. |
| Remove |  | 6 | HGI | HuntGroup ID | TLI |  | E06FLDH05517 | Required if TIP is populated. |

##### C03-2050 WISE "Contact Us" URL Modifications

Type: 4

Description:  This initiative will remove the “Contact the WISE Team” E-mail link and direct the CLEC to contact the NSC Help Desk to report system-related problems.

Business Rule Impacts:  None

Edit Impacts:  None

##### E03-0044 Modify E05/6FLDH02098 to make TC PER Optional on EU Form

Type:  4

Description:  Transfer of Calls Period (TC PER) will now be an Optional field.

Business Rule Impacts:

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | EU | 062 | Field Name: TC PER Usage FROM: Conditional TO: Optional |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | EU | 067 | Field Name: TC PER Usage FROM: Conditional TO: Optional |  |

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remove | 5 | 6 | EU | Disc Info | TC PER | E05FLDH02098 | E06FLDH02098 | Required if TC OPT populated. |
| New | 5 | 6 | EU | Disc Info | TC OPT | E05FLDH02143 | E06FLDH02143 | If TC PER is populated, position 1 of TC OPT must =C,S. |

##### E04-0001 Remove edits to make TC PER Optional for RS and DDPS forms

Type:  4

Description:  Transfer of Calls Period (TC PER) will now be an Optional field.

Business Rule Impacts:

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | RS |  | Field Name: TC PER Usage FROM: Conditional TO: Optional |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | RS |  | Field Name: TC PER Usage FROM: Conditional TO: Optional |  |
| Change | DDPS |  | Field Name: TC PER Usage FROM: Conditional TO: Optional |  |

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | New Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Remove | 5 | 6 | RS | Svc Det | TC PER | E05FLDH04208 | E06FLDH04208 | Required if TC OPT populated. |
| Remove |  | 6 | DDPS | Transfer of Calls Detail | TC PER |  | E06FLDH06635 | Required if TC OPT populated. |
| New | 5 | 6 | RS | Svc Det | TC OPT | E05FLDH04236 | E06FLDH04236 | If TC PER is populated, position 1 of TC OPT must =C,S. |
| New |  | 6 | DDPS | Transfer of Calls Details | TC OPT |  | E06FLDH06648 | If TC PER is populated, position 1 of TC OPT must =C,S. |

##### E04-0002 Modify edits for correct TOA values for Res Accts outside IL & SC

Type:  4

Description:  Modify error messages to be more descriptive for TOA values when Listings requested are for a Residence Account.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | DL | Listing Control | TOA | E05FLDH09615 | E06FLDH09615 | If position 1 of LSR TOS=2, EU STATE does not=IL,SC and LACT=N,I,Z then TOA must =R. |
| Change | 5 | 6 | DL | Listing Control | TOA | E05FLDH09791 | E06FLDH09791 | If LSR AR is not populated, position 1 of LSR TOS=2, EU STATE does not =IL,SC and LACT=O,D then TOA must –R. |

##### E04-0007 Modify REQTYP/ACT/LNA edits to match Form Level META Edits

Type:  4

Description:  Modifying the REQTYP/ACT/LNA edits

Details:  REQTYP=KB, ACT=C, LNA value of P is being removed.  Private Line accounts do not have a PIC established.

REQTYP=PB, ACT=W, LNA=W is being removed, when ACT=W, the Service Specific Forms are prohibited.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | REQTYP/ACT/LNA |  |  | E05METH10001 | E06METH10001 | REQTYP/ACT/LNA combination is not valid. |
| Remove | 5 | 6 | REQTYP/ACT/LNA |  |  | E05METH10001 | E06METH10001 | REQTYP/ACT/LNA combination is not valid. |

##### E04-0009 Modify E05/6FLDH09767 not to invoke for a PO Box Address

Type:  1

Description:  Modify edit to recognize LANO to not invoke when the customer wishes to publish a PO Box in their directory listing.

Business Rule Impacts:

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | DL | Listing Instruction | LANO | E05FLDH09767 | E06FLDH09767 | Required if any address field is populated, except when LASN=PO BOX or PO Box |

##### E04-0010 Remove/modify edits that will never invoke

Type:  4

Description:  Remove edits that will never invoke, modify edits to remove conditions that will never invoke.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | LS | Admin | ATN | E05FLDH03003 | E06FLDH03003 | Required if ACT = N,C,M,T,R,V. |
| Remove | 5 | 6 | LS | Svc Det | ECCKT | E05FLDI03033 | E06FLDI03033 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | NP | Admin | ATN | E05FLDH03303 | E06FLDH03303 | Required if ACT=N,V. |
| Change | 5 | 6 | LSNP | Admin | ATN | E05FLDH03603 | E06FLDH03603 | Required if LSR ACT=N,M,R,V. |
| Remove | 5 | 6 | LSNP | Svc Det | ECCKT | E05FLDH03660 | E06FLDI03660 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | LSNP | Svc Det | ECCKT | E05FLDI03661 | E06FLDI03661 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | LSNP | Svc Det | ECCKT | E05FLDI03662 | E06FLDI03662 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | RS | Svc Det | ATN | E05FLDH04003 | E06FLDH04003 | Required if LSR ACT=N,C,M,T,R,V. |
| Remove | 5 | 6 | RS | Svc Det | TNS | E05FLDI04121 | E06FLDI04121 | CLEC is not the Local Service Provider on the account. |
| Remove | 5 | 6 | RS | Svc Det | ECCKT | E05FLDI04132 | E06FLDI04132 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | RS | Svc Det | OTN | E05FLDI04128 | E06FLDI04128 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | PS | Admin | ATN | E05FLDH05003 | E06FLDH05003 | Required if LSR ACT=N,C,R,V. |
| Remove | 5 | 6 | PS | Svc Det | TNS | E05FLDI05111 | E06FLDI05111 | CLEC is not the Local Service Provider on the account. |
| Remove | 5 | 6 | RPL | Disc Info | DISC ECCKT | E05FLDI07151 | 06FLDI07151 | CLEC is not the Local Service Provider on the account. |
| Remove | 5 | 6 | RPL | Pri Loc Svc Det | ECCKT | E05FLDI07155 | E06FLDI07155 | CLEC is not the Local Service Provider on the account. |
| Remove | 5 | 6 | RPL | Sec Loc Svc Det | ECCKT | E05FLDI07167 | E06FLDI07167 | CLEC is not the Local Service Provider on the account. |
| Change | 5 | 6 | RFR | Admin | ATN | E05FLDH07503 | E06FLDH07503 | Required if LSR ACT=N,C,M,T,R,V. |
| Change | 5 | 6 | RFR | UNI Ckt Det | ECCKT | E05FLDH07508 | E06FLDH07508 | Required if ACT=C,M,T,R,V. |

##### E04-0011 Modify E05/6FLDH01252 to include ACT=T

Type:  4

Description: Modify edit to validate lines when ACT=T, error message will remain the same.

Business Rule Impacts:

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | LSR | Admin | LST | E05FLDH01252 | E06FLDH01252 | Maximum number lf lines ordered from Zone Density 1has been exceeded. |

##### E04-0012 Modify E05/6FLDH03124 to include Line Split

Type:  4

Description:  Modify edit to validate SLTN for Line Split accounts.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | LS | Svc Det | SLTN | E05FLDH03124 | E06FLDH03124 | If REQTYP=AB, ACT=N and position 2 of TOS does not=P then account defined by SLTN cannot be UNE-Platform or Line Split. |

##### E04-0015 Modify error messages for E05/6FLDH01477, 4245, 6128 and E06FLDH06650

Type:  4

Description:  Modify error messages to correct punctuation and meet character limitation.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | LSR | Admin | ATN | E05FLDH01477 | E06FLDH01477 | If REQTYP=AB, ACT=V, SLI=S, pos 2 of TOS=F, ATN is numeric & acct defined by ATN is not Line Split or UNE-Platform then multiple TNs cannot exist on account. |
| Change | 5 | 6 | RS | Svc Detail | FEATURE | E05FLDH04245 | E06FLDH04245 | If REQTYP=EB, ACT=C with any LNA=C,N,X or ACT=V, addr is in overlay, acct has any fiber lines and TNS is new or on fiber then IOSC must be fiber compatible. |
| Change | 5 | 6 | CRS | Station Detail | FEATURE | E05FLDH06128 | E06FLDH06128 | If REQTYP=PB, ACT=C with any LNA=C,N,X or ACT=V, addr is in overlay, acct has any fiber lines and TNS is new or on fiber then IOSC must be fiber compatible. |
| Change |  | 6 | DDPS | Feature | FEATURE |  | E06FLDH06650 | If REQTYP=NB, ACT=C with any TACT=C,N,X or ACT=V, addr is in overlay, acct has any fiber lines and TNS is new or on fiber then IOSC must be fiber compatible. |

##### E04-0020 Modify edits to allow Hunt Forms for PBX & DID/DOD

Type:  4

Description:  Edits are being modified to allow the LSOG 6 HGI form to be populated for PBX and DID/DOD accounts.

Business Rule Impacts:  None

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change |  | 6 | LSR | Admin | TOS |  | E06FLDH01260 | If HGI HA is populated, position 2 of TOS must =A,D,E,J,Q. |
| Change |  | 6 | HGI | Admin | PON |  | E06FLDH05501 | HGI form prohibited if position 2 of LSR TOS does not =A,D,E,J,Q. |

##### C03-1165 Allow Centranet Orders when ACT=V and existing profile is not Centranet

Type: 1

Description:  The Change Request will allow CLECs to convert an existing Centranet account to resold account.

Details:

Resale line converting to Centranet:

REQTYP=PB

ACT=V

LNA=V

AR=3

The system will allow the conversion account to be established as Centranet.

Centranet line converting to Resale:

REQTYP=EB

ACT=V

LNA=V

AR=4

The system will allow the conversion account to be established as resale.

Business Rule Impacts:

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | LSR/ Administration | 044a | Field Name: AR – Account Regrade Usage: From: Optional To: Conditional | To: 3 = Conversion account to be established as Centranet. 4 = Conversion account to be established as Resale. |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | LSR/ Administration | 051a | Field Name: AR – Account Regrade Usage: From: Optional To: Conditional | To: 3 = Conversion account to be established as Centranet. 4 = Conversion account to be established as Resale. |

Edit Impacts:

The following table depicts the edit changes associated with this change request:

| Action | LSOG Version | Form | Section | Field | LSOG 5 Error Code | LSOG 6 Error Code | Error Message |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Change | 5 | 6 | LSR | ADMIN | AR | E05FLDH01429 | E06FLDH01429 | If populated, valid values: 1,2,3,4. |
| Change | 5 | 6 | DL | Listing Control | LACT | E05FLDH09790 | E05FLDH09790 | If LSR AR=1,2 then at least one LACT must =D,O. |
| Change | 5 | 6 | LSR | ADMIN | TOS | E05FLDH01259 | E06FLDH01259 | If ACT=V,W, AR is not populated then non-coin customer profile must agree with position 1 of TOS and coin customer profile must agree with positions 1 and 2 of TOS. |
| Add | 5 | 6 | LSR | ADMIN | AR | E05FLDH01437 | E06FLDH01437 | If REQTYP not =PB or ACT not =V, or no CRS LNA=V then AR cannot =3. |
| Add | 5 | 6 | LSR | ADMIN | AR | E05FLDH01438 | E06FLDH01438 | If REQTYP not =EB or ACT not =V, or no RS LNA=V then AR cannot =4. |
| Change | 5 | 6 | LSR | Admin | REQTYP | E05FLDH01342 | E06FLDH01342 | PB not allowed for non-Centranet account. |
| Change | 5 | 6 | LSR | Admin | REQTYP | E05FLDH01343 | E06FLDH01343 | EB not allowed for Centranet account. |
| Change | 5 | 6 | EU | Disc Info | NAME | E05FLDH02109 | E06FLDH02109 | End User name does not match profile. |
| Change | 5 | 6 | EU | Disc Info | NAME | E05FLDH02110 | E06FLDH02110 | End User name does not match profile. |

##### C03-1811 Expand the number of characters in the NAME field for Order and CSI

Type: 1

Description:

Expand the character limitation in Order, LSOG 5 and LSOG 6 for the NAME field from 25 A/N characters to 28 A/N characters.

Business Rule Impacts:

The following table depicts LSOG 5 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | EU/ Location and Access | 008 | Field: NAME – Name Length: From: 25 To: 28* |  |

The following table depicts LSOG 6 Business Rule changes associated with this initiative.

| Action | Form or Transaction/ Section | Field # | Header Section | Valid Entry Section |
| --- | --- | --- | --- | --- |
| Change | EU/ Location and Access | 009 | Field: NAME – Name Length: From: 25 To: 28* |  |

Edit Impacts:  None