OSD Manual

Functions and Operation

# 1. On Screen Menu (OSD)

# 2. Setting up the menu

Settings can be made using the 5 way buttons locally and RS-485 wired remote control remotely.

1. Press the Button to access the SETUP mode.

The SETUP menu is displayed on the monitor.

2. Please select any function you wish to activate by using the UP/DOWN selections.

The arrow can be moved up or down by using the UP/DOWN selections.

Position the arrow to point to the function you wish to operate.

# 3. Adjust the selected feature by pressing LEFT/RIGHT selections.

# 4. When completed, move the arrow indicator to ‘EXIT’ and press the button to finish all settings.

# ☞ Note

# · If ‘      ‘ indication appears on a selected sub-menu, press the button to get into a following menu.

# · If ‘ --- ‘ indication appears on any sub-menu, it means the function with this mark is deactivated.

# (Ex : When SENS-UP is OFF, 3-DNR becomes deactivated ‘---‘ )

# 3. LENS

Select the lens and adjust the SETUP suitable to the type of lens.

◆ When DC lens is used. (※ Default)

1. Please select the lens mode to DC IRIS.

2. Press the SET to enter the <DC IRIS MENU>.

-  BRIGHTNESS: adjust the brightness of screen when the environment is

extremely bright or dark.

-  REACTION:     Reaction speed of the shutter is adjustable.

It is useful when the light condition of the environment keeps

changing quickly.

3.  Save

Press SAVE to finish all settings and return to <MAIN MENU>

◆ When MANUAL lens is used.

1. Please select the lens mode to MANUAL.

2. Press the SET to enter the <MANUAL IRIS MENU>.

-  BRIGHTNESS: same as above

-  REACTION: same as above

# 4. EXPOSURE

(1) AGC (Auto Gain Control)

- OFF: Deactivates the AGC function.

- LOW: Allows automatic gain control from 0 to 20dB. (※ Default)

- MIDDLE: Allows automatic gain control from 0 to 30dB.

- HIGH: Allows automatic gain control from 0 to 42dB.

※ The higher the gain level, the brighter the screen becomes while the higher the noise as well.

(2) SHUTTER

A.   AUTO: The shutter speed is controlled automatically. (※ Default)

B. FLK: Please select FLK mode when flickering occurs on the

screen, due to an imbalance between illumination and frequency.

C. FIXED : The shutter speed is controlled manually.

- You can select the speed from ‘1/60’ to ‘1/90,000 sec. (NTSC), ‘1/50’ to ‘1/90,000 sec. (PAL).

- You can select Digital Slow Shutter between  x2 ~ x512. (DSS)

※ Please use FIXED mode only when the light level of the surveillance area is fixed all the time.

(3) SENS-UP

- Low light sensitivity is greatly improved with the use of this function.

- Low light sensitivity level is adjustable from 2 to 512 times.

- When SEN-UP level is higher, the picture becomes brighter while noise is

increased at the same rate of SENS-UP.

ON : Adjustable SENS-UP level between  x2 ~ x512.

OFF: SENS-UP is disabled.

※ Default setting is <x8>

☞ Note

· When the SHUTTER is set to MANUAL mode, SENS-UP does not operate.

· When the AGC is set to OFF, SENS-UP does not operate.

(4) INITIAL SET

Initialize all settings of EXPOSURE menu.

(5) SAVE

# 5. DAY / NIGHT

It is used to improve the sensitivity and clarity of picture quality at low light.

- DAY      :  The image is always displayed in color.

- NIGHT :  The image is always displayed in black and white.

- AUTO1:  The image is automatically converted to B/W from Color at 3 lux.

● IR WDR LEVEL: Select  Anti- IR saturation level - OFF/LOW/MIDDLE/HIGH

● IR WDR ADJUST: Adjust the value in each of selected level - 0 ~ 6

- AUTO2: The image is automatically converted to B/W from Color at 3 lux.

· D/N LEVEL: LOW/MIDDLE/HIGH

· FILTER DLY:  Select the duration time about changing the Day/Night mode.

(1 SEC, 3 SEC, 5 SEC, 10 SEC, 15 SEC, 30 SEC, 60 SEC)

· NIGHT BURST: Burst ON/OFF selectable.

· INITIAL SET: Initialize all settings of AUTO2 menu.

# ※ Default setting

# - Infrared camera: AUTO1

# - Non-Infrared camera: AUTO2

# 6. WDR/BLC/ECLPS

# The image quality is greatly improved with the use of this mode when there is a strong backlight behind the object.

- OFF : Deactivates the WDR function.

- WDR: Camera scans both of bright lit background and shaded area distinctively

under an extremely contrasted light situation. (LOW/MIDDEL/HIGH)

- BLC: Enables a user to directly select a desired area from a picture and

to view the area more clearly.(LOW/MIDDEL/HIGH)

-ECLIPSE:

- Can mask the head lights to view car license number plate more clearly.

- Can select masking color.

- Adjust the ECLIPS level at the GAIN CONTROL as OFF mode.

# 7. White Balance (WHITE BAL)

This is useful to optimize the white balalnce control under a certain artificial lighting area where a standard white balance condition is not suitable.

- ATW (Auto Tracking White Balance)

This mode can be used within the color temperature

range of 1,500˚K~11,000˚K. (※ Default)

- COL-ROLL

Anti color rolling mode.

Use it only when the rolling is severely shown.

- MANUAL

Recommanded to use it when the light temperature is fixed all the time

Select INDOOR or OUTDOOR mode.

- PUSH (Push lock)

Use this when the White Balance is deviated.

Face the camera toward the white wall or white paper and press the Tact SW.

☞ Note

White Balance may not work properly under the following condition

- When the color temperature of the environment surrounding the subject is out of the

control range.(e.g. clear sky or sunset)

- When the ambient illumination of the subject is dim.

- If the camera is directed towards a fluorescent light or is installed in a place where

illumination change dramatically, the White Balance operation may become unstable.

8. 2D-DNR (2D Noise Reduction)

- LOW

- MIDDLE

- HIGH

- DISABLED: Deactivates 2DNR. Noise is not reduced.

- OFF : Activates 2DNR(Level : 0). Noise is not reduced.

☞ Note

<Bad pixel detection> function is operated only when <2D-DNR DISABLED> is selected.

# 9. 3D-DNR (3D Noise Reduction)

The background noise in the low light level decreases automatically

as the level of gain changes.

- DNR LEVEL

Adjust the noise reduction level.

- DESTINATION

Adjust the 3DNR gain.

- GLOBAL MOVEMENT

Control ghost phenomenon

# 10. EFFECTS

- D-ZOOM : You can use a digital zoom.

· ZOOM : x1 ~ x8.30

· DZOOM PAN : -100 ~ 100

· DZOOM TILT : -100 ~ 100

- IMAGE FREEZE : You can view still or live image.

- D-EFFECT

· V-FLIP : You can flip the picture vertically on the screen.

· MIRROR : You can flip the picture horizontally on the screen.

· ROTATE : You can flip the picture rotatively on the screen.

- CONTRAST : 0 ~ 100

- SHARPNESS : 0 ~ 100

- COLOR ADJUST

· COLOR  : ON/OFF

· COLOR LEVEL : 0 ~ 200

. COLOR HUE : -180 ~ 180

. RED GAIN : -100 ~ 100

. BLUE GAIN : -100 ~ 100

- TARGET CROSS : Display ‘╇’ on the screen

· COLOR  : BALCK,GRAY,WHITE,RED,GREEN,YELLOW

· MOVE X : -100 ~ 100

. MOVE Y: -100 ~ 100

. INITIAL SET

. SAVE

☞ Note

At TARGET CROSS function is in operation, ‘╇’  display shall disappear if MOTION DET function is ‘ON’

- BAD PIXEL: BAD PIXEL compensation

· BP DETECTION: Make the screen completely black by covering the camera.

· SEARCH AREA: X START/Y START/WIDTH/HEIGHT

. THRESHOLD: 40 ~ 1024

. SAVE

(※ Users may simply activate BP DETECTION and go directly to SAVE. Then Bad pixels in full screen are

compensated automatically)

- INITIAL SET : Initialize all settings of EFFECTS menu.

(※ TARGET CROSS and  BAD PIXEL modes are not initialized)

- SAVE

# 11. SPECIAL MENU

CAM NAME

- Please position the arrow to point to ’CAM NAME’ by using the

UP or DOWN selection.

- Please select ‘ON’ by using the LEFT and RIGHT selection.

Please press the button to complete ‘ON’.

☞ Note

If ‘OFF’ is selected, the CAM NAME does not appear on the monitor even if it has been input.

- Up to 15 letters are offered for the CAM NAME.

① Please move the cursor to the letter to choose by using the UP                                   and DOWN selections.

② Set an ID from A~Z /a~z /0~9 by using the UP, DOWN, LEFT                                      and RIGHT Selections.

③ Lock in the letters by using the button.

· When the letter is locked in, the cursor moves to the next space.

④ Please repeat the above to input CAM NAME.

☞ Note

· For a wrong name has been input,

- If you press the button after moving the cursor to CLR, all

letters will be erased.

- If you want to correct a letter, please move the cursor to the arrow at the bottom left of the

screen and press the button.

- Please position the cursor on the letter you wish to correct, and then move the cursor onto

the letter you wish to choose and press the button.

- When a name has been chosen, please select a position for the name to display.

① Please move the cursor onto ’POS’ and then press the button.

② The name will appear at the top left hand corner.

③ Please find the position you wish to display the name by using the 4 directional

selections, and then press the Button.

- Please select ‘END’ and then press the Button to complete CAM NAME input.

MOTION (Motion Detection: MD)

- ZONE NUMBER : You can select up to 8 MD areas.

- ZONE STATE : Determines whether to use the MD area selected in ZONE NUMBER.

- WIDTH : Determines the coordinate of the horizontal size.

- HEIGHT : Determines the coordinate of the vertical size.

- MOVE X : Determines the coordinate of the horizontal axis.

- MOVE Y : Determines the coordinate of the vertical axis.

- SENSITIVITY : Determines the coordinate of the sensitivity.

- INITIAL SET : Initialize all setting of MOTION DET menu.

- SAVE : Select this to save the MOTION menu setting and

return to the SPECIAL menu.

PRIVACY (Privacy Masking)

- MASK NUMBER : You can select up to 8 PRIVACY areas.

- MAKS STATE : Determines whether to use the selected in

AREA SELECT.

- SENSITIVITY : Determines area color. You can select GRAY,

WHITE, RED, GREEN, BLUE, YELLOW, BLACK.

- WIDTH : Determines the coordinate of the horizontal size.

- HEIGHT : Determines the coordinate of the vertical size.

- MOVE X : Determines the coordinate of the horizontal axis.

- MOVE Y : Determines the coordinate of the vertical axis.

- INITIAL SET : Initialize all setting of PRIVACY menu.

- SAVE : Select this to save the PRIVACY menu setting and return

to the SPECIAL menu.

LANGUAGE

You can select the menu language according to your requirements.

- English, Korean, Russian, Spanish, French

STABILIZER  (DIS)

This function mitigates any picture movement due to external factors

such as wind.

☞ Note

· The chance of resolution decrease is existed because  STABILIZER

function uses the digital zoom.

· STABILIZER doesn’t operate when background illumination is too low.

· STABILIZER doesn’t operate when object pattern is monotonic like  sky or white wall.

MONITOR TYPE

- CRT : GAMMA 0.45

- LCD : GAMMA 1.0

FACE REC (Face Recognition)

A special area where the internal illumination is dark while strong back light exists behind the object, normally human face becomes unrecognizable. This mode is suited for this particular situation.

- FR BRIGHTNESS : 0 ~ 40

- FR CONTRAST : 0 ~ 40

- COLOR SAT : 0 ~ 200

- CONTRAST : 0 ~ 100

- OUTPUT LEVEL : -64 ~ 64

- SHARPNESS : 0 ~ 100

COMM SET (Communication seting)

This function sets up the camera communication status when controlling the camera

through an external control device.

- CAMERA ID

· CAMERA ID : Determines the camera’s identification

number (between 0 and 255).

·  ID POSITION: Displays camera title on top left & right side of

the screen.

· BAUD RATE :  You can select 4800/9600/19200/38400/57600 bps .

· SAVE/REBOOT: Select this to save the COMM SET menu setting and  return to

the main screen.

·  PREVIOUS: Return to COMM SET menu.

☞ Note

-  RS-485 cable : Please connect (-) firstly and then (+).

-  IF there happens RS-485 cable conection error or any other problems, a message

‘ERROR RS-485 Connection. Please Reconnect and Reboot’ is displayed.

Please reset the power or OSD.

FACTORY RESET

Resets the camera setting to the factory defaults.

But  <COMM SET> menu is not initialized.

12. EXIT

Save all setting menus by pressing the Tact SW and then exit by pressing EXIT menu.

# Text boxes

How to use OSD button (Tact SW)

- Press

- to enter the menu

- to save settings

- Push up or down

- to select functions

- Push left or right

- to adjust a level or mode of sub-menu