## Table of Contents

Table of Contents	2

Introduction	5

Disclaimer	5

Section 1 – Background Information	6

1.1. Introduction	6

1.2. Purpose	6

1.3. Collapse of the Iron Curtain	7

1.4. The Aircraft	7

1.5. The Fuel System	9

1.6. The Control Panel	10

Section 2 - Technical Information	11

2.1 Performance	11

2.2 Dimensional Characteristics of the Yak 18T	11

2.3 Fuel Specification and Octane Number	13

2.4 Carburettor	13

2.5 Fuel Pressure in front of Carburettor	13

2.6 Petrol Pump	13

2.7 Fine Filter	13

2.8 Oil Grade	13

2.9 Oil Consumption	13

2.10 Oil Pressure	13

2.11 Oil Inlet Temperature	13

2.12 Cylinder Head Temperature	13

2.13 Magnetos	13

2.14 Spark Plugs	13

2.15 Propeller	14

2.16 Main Flight Performance at Standard Conditions	14

2.17 Airfield Performance	14

Section 3 – Operational Limitations	15

3.1. Flying Limitations	15

3.2. Operational Loading	15

3.3. Crosswind Components	15

3.4. Weight and Balance Data	15

3.5. Other Limitations	16

Section 4 - Pre-flight Inspection	17

4.1. Preliminary Pre-Flight Actions	17

4.2. Relevant Documentation	18

4.3. Performing the Inspection	19

Section 5 – Engine Start Preparation	27

5.1. Hydraulic Lock/Shock Avoidance	27

5.2. What is Hydraulic Lock/Shock?	27

5.3. The Consequences	27

5.4. What can be done?	28

5.5. Other Solutions	28

5.6. Conclusion	29

Section 6 – Engine Start	30

6.1. Prior to Starting the Engine	30

6.2. Avoiding Hydraulic Shock	30

6.3. Engine Priming	30

6.4. Engine Starting	31

6.5. Engine Warm-up	32

6.6. Taxiing to the holding point	33

6.7. Engine Run-up	34

Section 7 - Flying	36

7.1. Take-off Preparation	36

7.2. Take-off and Climb	36

7.3. Cross-Wind Take-Off	37

7.4. Climbing	38

7.5. Engine Overheating (During the Climb)	38

7.6. Horizontal Flight	39

7.7. Chips in Oil	40

Section 8 – Aerobatic Flight Manoeuvres	41

8.1 Steep Turn: 45° of bank	41

8.2 Steep Turn: 60° of bank	42

8.3 Figure Eight	43

8.4 Combat Turn	44

8.5 Diving	44

8.6 Steep Climb/Zoom	44

8.7 Spiral	45

8.8 Slipping	45

8.9 Slow/Barrel Rolls	46

8.10 Flick/Snap Rolls	46

8.11 Half-roll	47

8.12 Normal Loop	47

8.13 Half-Loop and Half-Roll	48

8.14 Aircraft Behaviour at Large Angles of Attack and Stall	49

Section 9 - Spins	51

9.1. Entry into spin	51

9.2. Spin Recovery	52

9.3. Recovery from an Inverted Spin	53

9.4. Unintentional Snap or Fall into Spin	53

Section 10 - Landing	55

10.1. Descent and Landing Preparation	55

10.2. Planning the approach	55

10.3. Going Around	56

10.4. Landing	56

10.5. Crosswind Landing	57

10.6. Engine Shutdown	57

Section 11 - Special Cases in Flight	59

11.1. Pilot Actions in case of Engine Failure	59

11.2. Pilot Actions in case of Pressure Drop	59

11.2.1. Engine Failure and the Primer	59

11.2.2. Pilot Actions in case of drop in Engine Oil Pressure	60

11.3. Pilot Actions in case of drop in Fuel Pressure and Non-Uniform Fuel Consumption	60

11.4. Pilot Actions in case of Engine Vibration	60

11.5. Pilot Actions in case of Propeller Over-speeding	61

11.6. Pilot Actions in case of in-flight Fire	61

11.7. Pilot Actions in case of Forced Landing	61

11.8. Pilot Actions in case of Emergency Undercarriage Extension	62

11.9. Pilot Actions in case of Emergency Flap Extension	62

11.10. Landing with the Flap Retracted	63

11.11. Pilot Actions in case of Brake Failure	63

11.12. Pilot Actions in case of Radio Station Failure	63

11.13. Pilot Actions in case of Generator Failure	63

11.14. Pilot Actions in case of Converter Failure	64

11.15. Pilot Actions in case of Speed Indicator Failure	64

11.16. Pilot/Crew Actions in case of a Emergency Bailout	64

11.17. Pilot Actions for Engine Hand Starting	65

11.18. Special Feature of the Power Unit at low ambient temperatures	66

Section 12 - Operation of Systems and Equipment	67

12.1 Radio Station	67

12.2 Radio Compass	67

12.2.1 General Information	67

12.2.2 Pre-flight radio compass switching-in, tuning and checking	67

12.2.3 Radio Compass Usage in Flight	68

12.2.3.1	Compass System	70

12.2.3.2	Pre-Flight Compass Switching-on	70

12.2.3.3	Troubles and failures of the Gyro-magnetic Compass	71

12.2.3.4	Magnetic Compass	72

12.2.3.5	Gyro-horizon	72

12.2.4 The Heating and Ventilation System	77

12.2.5 Aneroid and diaphragm actuated instruments and the pitot static systems	77

12.2.6 Operational Limitations	78

12.2.7 Light Facilities	79

Index	81

## Introduction

This manual is to be used as a general guide for owners and pilots to understand and become familiar with Yak 18T Flight Operations.  Flying acquaintances can also make use of it as an initial education prior to practical experience.  This document is based on two versions of translated Russian flight operations manuals.  They were brought together in this single document with diagrams and images where appropriate.

The main purpose of this guide is to present the reader with pertinent information, experiences and wisdom about the Yak 18T.  If you have information that should be included in this manual, either identified as an obvious omission or as a useful enhancement, then kindly contact Alex Berry by email at alexberry@yak-aviation.com.  This document is up for review by Yak 18T owners and pilots.

The Yak 18T aircraft was initially designed for training Aeroflot pilot cadets.  It was purposely designed and manufactured as a robust but flexible 4-seat touring aircraft with the added bonus of aerobatic capabilities.  In recent times, many of these aircraft have been brought back to life via a complete overhaul both mechanically and cosmetically, with custom paint schemes, up rated engines and executive leather interior being commons options.  For these reasons, and many more, the Yak 18T is a serious contender for the discerning pilot who is seeking both aerobatic capability and, with extended fuel tanks, good touring capacity.

The 18T is worthy of all due consideration, especially when value for money is a key factor in the decision to purchase a recently overhauled aircraft.  The 18T is considered a complex aircraft; it has a 360HP 9-Cylinder M-14P radial engine with both Retractable Gear and Variable Pitch Propeller, clearly not your average PA-28 or C172.  The engine demands care and respect like any other engine, but it may be somewhat different to what you are used to, or what you trained in.  However, do not let this dissuade until you have all the facts and have had a much closer look at this charismatic type.

Many modifications for the 18T are currently available.  For example, the engine can be up rated to 400HP, the propeller can be exchanged for a 3-blade German MTV-9 240/250 (amongst others), inverted fuel and oil systems, extended wing tip and extended wing tanks can also be fitted.  This manual does not however take into account the majority of these modifications – although we would be happy to incorporate these sections should they become available.

This manual contains instructions on Yak 18T piloting technique and general flight operations on the ground and in-flight.  The checks in this guide also assume that only one person is present, the Pilot-in-Command (PIC).

### Disclaimer

This flight operations manual is for guidance purposes only and has not been officially approved by Yakovlev or any other authority.  It is not “a” or “the” definitive guide to Yak 18T Flight Operations and no claim is made to this effect.   The originator of this document will not be held responsible for any action taken as a result of information presented herein.

Your support and assistance with the content and accuracy of this manual will no doubt aid all Yak 18T owners in continuing to conduct safe and informed flights.

## Section 1 – Background Information

This section contains a brief background that was largely extracted from an article by A. Dugin (Smolensk) titled “YAK 18T. LIFE GOES ON”.

### Introduction

The 25th anniversary of the first Yak 18T take-off at the Smolensk Aircraft Manufacturing Plant was celebrated on May 25th, 1999.  Today, the Yak 18T is the most popular general aviation aircraft in the Commonwealth Independent States (CIS) countries.

It is well-known to all aviators of the CIS countries, developed by the Yakovlev Design Bureau and followed the Yak-18U, Yak-18A, Yak-18P, Yak-18PM and Yak-18PS.  The 18T was the final modification in the Yak-18 family.  The two-seater basic aircraft Yak-18 (1946) was put into production in 1947-1955 at the Arsenyevsk and Kharkov Aircraft Manufacturing Plants as well as in China. 3,752 and 379 aircraft were built in the USSR and China respectively.  The Yak-18U (1953) is an improved two-seater trainer.  During the period of 1954-1957 960 Yak-18U were put out at Arsenyevsk Aircraft Manufacturing plant. The Yak-18-A (1957) was produced from 1957 till 1961 at Arsenyevsk Aircraft Manufacturing Plant (927 aircraft) and 1,796 planes were made in China.  In 1961-1962, 125 aircraft were put out at Arsenyevsk Aircraft Manufacturing Plant. The Yak-18PM (1966) is aerobatic. In 1970-1972, 25 aircraft were produced in Arsenyevsk.  The Yak-18PS (1970) is aerobatic too but there is no information about the number of aircraft produced (according to Russian Publishing Company Kodeks and KONVERSULT Consulting Company database).

### Purpose

At first, the Yak 18T was designed to be multi-purpose.  That's why the Ministry of Timber Industry and the Ministry of Public Health ordered 300 aircraft each (unfortunately their requests were not met).  According to the USSR Council of Soviet Ministers (SOVMIN), the Yak 18T became a trainer for the Civil Aviation schools, so that the production program was intended only for the Ministry of Civil Aviation.

For ten years the Smolensk Aircraft Manufacturing Plant sent its output to Aktubinsk, Buguruslanovsk, Kirovograd, Krasnokutsk, and Sasovsk Civil Aviation schools. The Yak 18T’s were not delivered to the DOSAAF (semi-military organisations) airclubs.

Only a "go-ahead" Ivanovsk airclub managed to get 10 aircraft.  All-in-all 536 Yak 18T were produced in Smolensk for the period of 1973-1983, including experimental and prototypes.  In 1974 an ambulance aircraft was built.  Its purpose was to transport a patient on a stretcher with the escort of a doctor.  But the series production of this configuration was not organized.  Also, versions of an aircraft with ski and floating landing gears were being developed at the Yakovlev Design Bureau.  But everything was in vain. Nothing came out of it.

The schools mastered the Yak 18T well while using it.  All the shortcomings of the design were eliminated and improved according to 217 bulletins.  But in 1988 according to the decree of the Ministry of Civil Aviation (MCA) of the USSR all the aircraft were taken out of operation and subjected to discarding, even though the aviation industry produced nothing comparable to replace the Yak 18T.  Absolute nonsense!  For example, in Kirovograd plant, a team of workers, having completed the up-dating according to the bulletins, as it had been planned, signed their names in the logbook of the aircraft, which next morning was carried away for good. All aircraft fleet was replaced by the An-2 at the schools.

The students had to study the nuts and bolts of training flights "in a Kamaz instead of Zhyguli" (which means dump truck and automobile respectively) was a witty remark of one of the pilot instructors.  Part of the worn off Yak 18T was utilized.  But after the interference of a newly created USSR Federation of Amateur Aviators, DOSAAF workers and motorcar enthusiasts were held to ransom aircraft for the depreciated cost.  The nimblest managed to get the condemned for scrap-iron aircraft for 500…800 soviet roubles each or even for nothing. Thanks to such a decision more than 200 aircraft became privately owned property. As for the YAK 18T, it turned out to be the first popular General Aviation aircraft in the CIS countries. But, unfortunately, it is almost the only one up to the present day.

### Collapse of the Iron Curtain

After the "iron curtain" collapsed, this aircraft attracted the attention of foreign countries. Apparently, the aircraft participation in widely advertised flights of the crews of the Russian Federation of Amateur Aviators to the USA and Australia boosted its popularity.  The aircraft were taken abroad in different ways.  That's why at the present time the habitat of the aircraft spread to various countries from Bulgaria to New Zealand.

In 1993, the Smolensk Aircraft Manufacturing Plant resumed Yak 18T production.  Although the rigging was made afresh, the aircraft structure did not change.  Outwardly the second-generation aircraft differs by symmetrical installation of two footboards (footboards of the first-generation aircraft were mounted only on the left side).  Little changes also occurred in the equipment make-up. The ARK-9 was replaced by the ARK-15M.

The Ulyanovsk Civil Aircraft Academy (UCAA), the former Civil Aviation Centre of the Council of Mutual Economic Assistance, became the biggest customer of the second-generation aircraft.  Having got their bearings, the UCAA supervisors made a decision to get involved in primary training and bought 15 Yak 18T in Smolensk.  And here is the result: if other schools go on using the An-2 as a trainer, and have been handing over certificates about completing the theoretical course instead of pilot license, in Ulyanovsk the students fly as much as they are supposed to.

### The Aircraft

The aircraft fuselage is mainly of riveted structure.  Glue-welded joining of stringers and skin is used in the rear part.  The wing is two-spar, cantilevers are mounted to the centre-section by the joint of the "lug-plug" type with four bolts each.  The wing centre-section is made as a one-piece unit with a fuselage and the wingspan is 3.6m (11ft). That puts certain limitations on ground transportation.  Along the whole span of the centre-section to the lower berth of the rear spar, the landing dashboard is hanging. The frame of the wing and tail unit is all-metal.  Wing panels, ailerons, fin, stabilizer, elevator and rudder have aircraft cotton fabric ÀÌ-93 skin, which is called ‘percale’ in Russia, although these are different materials that can be used.

The cabin is four-seat.  Along the cabin sides there are two car-type doors from 850 to 1250mm in size, equipped with an emergency fault mechanism that allows the doors to be jettisoned in an emergency.  In the first row there are two armchairs, adjustable vertically and horizontally with the mechanism of shoulder belts tightening.  There is a passenger couch in the second row. Behind it there is an upper baggage rack and under it is quite a substantial baggage compartment. The hatch of the baggage compartment is to the left side of the board of the fuselage. The hatch lid opens up. And when it is closed, it is held by a pintle lock.  Access to the lock-knob is from the cabin side with a rack-back position of the couch.

There is a heating system, in which the outward air is heated from a heat exchanger of the engine exhaust and comes into the cabin. The system insures the windshield blower of the canopy.  The air-cooling system ensures the cabin pressurization under the velocity head influence (air intakes are located on both sides of the fuselage and on the canopy upper frame).  Left windshield is provided with an electric drive windshield wiper.  The service ceiling is 5,520m (16,730 ft).  But as oxygen system is not available on-board, it is not permitted to fly higher than 4,000m (13,120 ft) as it is stated later in this Flying Operations Manual (FOM).

The power plant consists of the M-14P engine and a variable-pitch propeller V530TA-D35 with an rpm governor R-2. It is completely identical to the propeller group of the Yak-52s, except for some little differences in engine mounting.  The tricycle-equipped landing gear with the nose strut is retractable.  The front strut wheel is castor.  The main landing gear wheels have block brakes.  All landing gears are of telescopic type with a oleo-pneumatic shock-strut (AMG-10 oil and nitrogen).  The double action shock struts are used in the Yak 18T.  They ensure overcoming of the unpaved runway roughness with a smaller loading for frame construction.  The tire pressure is 3 kgpcm² (61lbpsq.ft).  A skilled pilot can turn the aircraft around practically on one wheel.  The turning radius equals the landing gear tread width.  A parking brake system is provided for the Yak 18T.  In the case of the main system failure, the emergency system can perform all the functions except for the M-14P start. The capacity of a main air system cylinder is 12l (3.2 gal), the emergency one is 3l (0.8 gal). During the flight the air system is recharged from the AK-50T compressor, mounted on the engine.

1. Propeller

2. M-14P engine

3. Oil tank

4. Pilot chair

5. Radio equipment

6. Landing light

7. Fuel tank

8. Retractable landing gear

The fuel (standard version) is distributed in two main tanks with the capacity of 95l (25 gal) each and in the service tank with the capacity of 3.5l (0.9 gal). The fuel is fed by gravity from the main tanks to a service tank, located in wing panels. The service tank is mounted lower than the main ones. The fuel is fed from the service tank, mounted on the engine by the 702K rotary pump.  Before the engine start-up a fuel priming pump is used for priming its cylinders and the 702K fuel pump.  The fuel to be used is B-91/115 gasoline, GOST (State All-Union standard) is 1012-72. But Voronezh Mechanichal plant is going to use the automobile AI-92 gasoline for the M-14P operation in the nearest future.

The oil system ensures oiling and cooling of rubbing surfaces of the engine parts as well as the P-2 regulator pump. The MS-20 oil of GOST 21743-76 is used in it. The oil circulation in the system is forced by the MN-14 gear pump, mounted on the engine. The oil tank is mounted on frame No 0. Its capacity is 24 l (6.35 gal). The air-oil cooler 2281-2-0 of a tubular type is mounted on the right side of the center-section of the front spar. Its air intake is located in the wing leading edge flap. To make the engine start-up easy in winter the system of oil thinning by gasoline is provided.

The Yak 18T inherited the ability to perform a full complement of aerobatics from the early aircraft of the "T" family. There is only one point to pay attention to. The standard oil system design doesn't provide the engine oiling during the inverted flight. That's why the FOI forbids its performing. The fuel and oil consumption doesn't exceed 45 lph (12 galph) and 1 lph (0.26 galph) respectively at the second cruising regime.

Three power supply systems are used on the Yak 18T. They are: a direct-current of a voltage of 28V, an alternate single-phase current of a voltage of 115V with frequency of 400 Hz and alternate three-phase current of the voltage of 36V and frequency of 400 Hz. The primary system is a direct-current system with the GSR-3000M generator and the 20NKBN-25UZ storage battery. The sources of alternate current are the PO-250A (115V) and the PT-200Ts (36V) converters.

### The Fuel System

| 1 - oil dilution valve | 10 - fuel drain valve |
| --- | --- |
| 2 - P-1B fuel pressure transmitter | 11 - vent pipe |
| 3 - oil feed pipe | 12 - check valve |
| 4 - main fuel tank | 13 - 740400 hand primer pump |
| 5 - service tank | 14 - fill hoses |
| 6 - main fuel tank | 15 - bypass pipeline |
| 7 - filler | 16 - fuel fire shut-off valve |
| 8 - fuel quantity transmitter | 17 - fuel filter |
| 9 - overflow and vent line | 18 - overflow and vent line of a service tank |

The standard complete set of aircraft instrumentation consists of the GMK-1AE compass system (CS), the AGD-1K gyro horizon, the EUP-53U turn indicator, the UC-450K airspeed indicator, the VD-10K altimeter, the VR-10MK VSI rate-of-climb indicator, the AM-10K accelerometer, the AchC-1 aircraft clock, the KI-13K magnetic compass, the SSKUA-1 angle-of-attack warning system.

### The Control Panel

| 1 - engine start button | 12 - US-450 speed indicator | 23 - EUP-53U indicator |
| --- | --- | --- |
| 2 - 2M-80 air system gauge | 13 - 1122-B horizon indicator | 24 - TUE-48 temperature indicator |
| 3 - AM-1OK accelerometer | 14 - VR-1MK rate-of climb indicator | 25 - TTsT-1 temperature indicator |
| 4 - landing gear warning light | 15 - MV-1bV pressure vacuum gauge | 26 - SBES-2077B fuel quantity indicator |
| 5 - PM1-1 magneto switch | 16 - ground break-down control button | 27 - ARK-15 control panel |
| 6 - hand primer pump product No 740400 | 17 - VD-1OK altimeter | 28 - KM-8 compensator |
| 7 - T6-U2 signal panel | 18 - SSLUA-1 system indicators | 29 - fuel emergency shut-off cock handle |
| 8 - GMK-1AE control panel | 19 - UKZ-1 indicator | 30 - Baklan-5 control desk |
| 9 - | 20 - PTE-1 tachometer indicator | 31 - landing gear emergency release cock |
| 10 - SPU-9 control panel | 21 - VA-Z voltammeter | 32 - electrical system charging cock |
| 11 - YGR-4UK indicator | 22 - AchS-1K clock | 33 - AZRGK-2 break-down signalling |

The radio equipment consists of the Baklan-5 radio compass and the MRP-56P station and the SPU-9 intercom. The radio navigational equipment includes the ARK-15M automatic marker receiver.

The RV-5 low-altitude radio altimeter and the Os-1 device for automatic landing were additionally installed on five aircraft for Kirovograd flying school some years ago. But Soviet GPS for the Yak 18T was unclaimed. So the aircraft of such a complete set haven't been produced any more.

For the night flights and in conditions of low visibility the red highlight of the dashboard and the control panel is provided. Besides the navigation lights and the MSL-3 signal beacon, the exterior lighting equipment includes the LFSM 28-200-landing/taxi light.

## Section 2 - Technical Information

This section contains some technical information about the performance, dimensional characteristics and standard equipment of the Yak 18T.

### Performance

| Engine | 360HP, M-14P |
| --- | --- |
| Engine starting system | Pneumatic |
| Cylinders | 9, Radial, Star-type/single layer |
| Cubic capacity | 10 litres (1.1l per cylinder) |
| Cooling system | Air |
| Weight (dry) | 214kgs ±2%, 471lbs ±2% |
| Max engine speed | 101% |
| Empty weight | 2,728lbs, 1,240kg |
| Gross weight | 3,630lbs, 1,650kg |
| Average cruise | 200km/h, 108kts, 124mph |
| Top speed (sea level) | 262km/h, 141kts, 162mph |
| Max. IAS (straight and level flight) | 300km/h, 162kts, 186mph |
| Max. IAS (straight and level flight with bumpiness) | 360km/h, 194kts, 224mph |
| Max. IAS (in a dive) | 460km/h, 248kts, 285mph |
| Range, 193litres (std. no reserve) | 760km, 470miles, 3hrs 45mins |
| Range, 193litres (+30mins reserve) | 660km, 410miles, 3hrs 15mins |
| Range, 193litres (+45div. + 30mins reserve) | 510km, 315miles, 2hrs 30mins |
| Range, 320litres (ext. no reserve) | 1,250km, 775miles, 6 hrs 20mins |
| Range, 320litres (+30mins reserve) | 1,150km, 714miles, 5 hrs 50mins |
| Range, 320litres (+45div. + 30mins reserve) | 1,000km, 620miles, 5 hrs 5mins |
| Ground run | 1,221ft, 370m |
| Ground roll | 1,155ft-1,551ft, 350m-470m |
| Service ceiling (with supplemental oxygen) | 16,400ft, 5,000m |
| Service ceiling (without supplemental oxygen) | 13,120ft, 4,000m |

The ranges above are based on an approximate average burn rate of 50 litres per hour of flight at 200km/h i.e. Cruise I.  Monitor the fuel burn rate of your particular aircraft against these figures (it may be more or slightly less) and always err on the side of caution.  Also note the additional ground run and roll distances based on take-off weight, fuel load, C of G, runway slope, icing conditions etc.  Never conduct flights purely based on the figures stated above.

### Dimensional Characteristics of the Yak 18T

###### General Data

| Length | 8.39m ±1.6cm (27’6”) |
| --- | --- |
| Height | 3.4m (11’1”) |
| LG wheel track | 3.12m ±2cm (10’2”) |
| LG wheel base at rest | 195.5cm ±0.6cm |
| Tyre size (braked wheel tyres of main undercarriage legs) | 50*15cm |
| Tyre size (nose undercarriage leg) | 40*15cm |
| Distance from tip of propeller blade to the ground (at parking position with compressed shock struts and wheel tires) | 16cm |
| Pitch angle at rest | 2° |

###### Wing

| Section | Klark YH |
| --- | --- |
| Area, Span | 18.8m², 11.16m (36’7”) |
| Length of mean aerodynamic chord | 1.74m (5’8”) |
| Aspect ratio | 6.6 |
| Dihedral (along ¼ chord line) | 7°20’ |
| Angle of wing setting | 2° |
| Ailerons area | 1.92m² |
| Aileron deflection (up/down) | 22°-1° / 15°-1° |
| Landing split flap area | 1.6m2 |
| Deflection angle of the landing split flap | 50° +3° / -1°30’ |

###### Horizontal Tail

| Area | 3.185m² |
| --- | --- |
| Span | 3.54m (11‘7”) |
| Elevator area (incl. trim tab) | 1.235m² |
| Dihedral | 0° |
| Elevator deflection (up/down) | 25° -1°30’ / 25° -1°30’ |
| Elevator trimmer deflection (up/down) | 20° +3°40’ / 20° -1°15’ |

###### Vertical Tail

| Area | 1.7m² |
| --- | --- |
| Rudder area | 0.982m² |
| Rudder deflection (left/right) | 27°-1° / 27°-1° |

###### Engine Conditions

| Engine Condition | Power nr. Ground (HP) | Crankshaft Speed | Supercharger pressure, mm mercury column | Specific fuel consumption g/l, s.hr |
| --- | --- | --- | --- | --- |
| Take-off regime | 360-2% (reduced) | 99-4% ground 99+1-2% air | Po+125±15 | 285-315 |
| Nominal I | 290-2% (reduced) | 82%-84% | Po+95±15 | 280-310 |
| Nominal II | 240-2% (reduced) | 70% | Po+75±15 | 265-300 |
| Cruise I | 0.75 of the measured power at Nominal II | 64% | 735±15 (absolute) | 210-230 |
| Cruise II | 0.6 of the measured power at Nominal II | 59% | 670±15 (absolute) | 215-235 |
| Idling |  | ≤ 26% |  |  |

- Higher power limit and boost pressure behind the supercharger at take-off, Nominal I and II is not limited

- 99.4% of the crankshaft rotational speed corresponds to 2900rpm

- Time of continuous engine operation in the take-off regime must not exceed 5mins at peak rpm conditions are 1min at rest conditions

| Maximum engine speed (rpm) | 101% |
| --- | --- |
| Idling (26%) to take-off regime engine acceleration capacity at V=0, H=0 does not exceed | 3 seconds |
| Maximum over-speeding at acceleration application in flight (duration does not exceed 1 second and time during service life – 30 minutes) | 109% |

### Fuel Specification and Octane Number

| Petrol | B-91/115 |
| --- | --- |
| Gost | 1012-72 (octane number ≥ 91) |

### Carburettor

| Symbol | AK-14P |
| --- | --- |
| Type | Pressure carburettor, without float |
| Inlet temperature | +10°C - +45°C |

### Fuel Pressure in front of Carburettor

| At operating conditions | 0.2-0.5 kgf/cm² |
| --- | --- |
| At minimum rpm at least | 0.15 kgf/cm² |

### Petrol Pump

| Symbol | 702 ML |
| --- | --- |
| Type | Lobe rotary pump |
| Number per engine | 1 |

### Fine Filter

| Symbol | 8D 2.966.064 |
| --- | --- |
| Type | Sump, gravity filter |
| Filtration fineness | 36-40(m |

### Oil Grade

| For flight and winter ops. | MC-20 or MK-22 (Gost 10103-49) |
| --- | --- |

### Oil Consumption

| At Cruise I (g/l sec/hr) | ≤ 8 (during 1st overhaul) |
| --- | --- |

### Oil Pressure

| At operating conditions | 4-6 kgf/cm² |
| --- | --- |
| At minimum rpm (in the main line) | ≥1 kgf/cm² |

(Measured through a special pipe connection at the oil pump)

### Oil Inlet Temperature

| Recommended | 50°C - 65°C |
| --- | --- |
| Minimum permissible | 40°C |
| Maximum during long term operations | 75°C |
| Maximum temperature in first 15mins operation | 85°C |

### Cylinder Head Temperature

| Recommended | 140°C - 190°C |
| --- | --- |
| Minimum permissible for engine normal operation | 120°C |
| Minimum for continuous operation | 140°C |
| Maximum for continuous operation | 220°C |

### Magnetos

| Symbol | M9-25M |
| --- | --- |
| Type | Four-spark, shielded |
| Number in the engine | 2 |

### Spark Plugs

| Symbol | CD-49CMM |
| --- | --- |
| Number per cylinder | 2 |
| Ignition sequence | 1-3-5-7-9-2-4-6-8 |

### Propeller

| Symbol | V530TA-D35 |
| --- | --- |
| Type | Variable-pitch tractor |
| Action | Direct |
| Direction of action | Left |
| Diameter | 2.4m (7’10”) |
| Blades | 2 |
| Minimum blade angle at 1000mm radius | 14°30’±10’ |
| Maximum blade angle at 1000mm radius | 14°30’±10’ |
| Range of blade rotation | 20°±40’ |
| Weight | 40kg+2% (88lbs+2%) |

### Main Flight Performance at Standard Conditions

| Maximum indicated horizontal airspeed | 262km/h, 141kts 162mph |
| --- | --- |
| Maximum service ceiling | 13,120ft, 4,000m |

As standard oxygen equipment is not available in the aircraft, flights at altitudes above 4,000m (13,120ft) are PROHIBITED.  In order to avoid the engine overheating, the climb to 3,000m (9,900ft) should be made at Nominal II (70%) conditions -

- V(limit) = 170km/h (91kts) at ambient temperature near the ground up to +20°C

- V(limit) = 180km/h (97kts) at ambient temperature near the ground over +20°C

Climb from 3000m and higher is allowed to be performed at Nominal I conditions V(limit) = 165km/h (89kts).  Time to climb to an extreme high altitude is ≤35 minutes.

### Airfield Performance

| Take-off Weight | Rotation Speed | Take-off Run | Take-off Distance to 10m (33ft) | Length of Aborted Flight | Touch-down Velocity with Flap | Landing Run | Landing Distance from 15m (50ft) |
| --- | --- | --- | --- | --- | --- | --- | --- |
| At mean conventional bearing power of soil 8-9 kgf/cm² |
| 1,650kg | 135km/h | 370m | 670m | 850m | 130km/h | 470m | 790m |
| 1,510kg | 125km/h | 265m | 540m | 650m | 120km/h | 390m | 690m |
| 3,637lbs | 73kts | 1,214ft | 2,198ft | 2,789ft | 70kts | 1,542ft | 2,592ft |
| 3,329lbs | 67kts | 870ft | 1,772ft | 2,132ft | 65kts | 1,279ft | 2,264ft |
| At mean conventional bearing power of soil 4-5 kgf/cm² |
| 1,650kg | 125km/h | 500m | 920m | 700m | 125km/h | 350m | 650m |
| 1,510kg | 120km/h | 455m | 830m | - | 124km/h | 350m | 610m |
| 3,637lbs | 67kts | 1,640ft | 3,018ft | 2,297ft | 67kts | 1,148ft | 2,132ft |
| 3,329lbs | 65kts | 1,493ft | 2,723ft | - | 67kts | 1,148ft | 2,001ft |

Landing without the extended split flap is permitted in the following cases:

- at headwind speed of less than 10m/s (19kts/22mph)

- at crosswind

- in case of faulty flap extension mechanism

- in the cases where the pilot possesses adequate skill

- in the case of aircraft ditching

## Section 3 – Operational Limitations

### Flying Limitations

| Maximum allowable indicated airspeed at diving | 300km/h | 162kts |
| --- | --- | --- |
| Maximum allowable indicated airspeed at turbulence (210-250km/h recommended) | 300km/h | 162kts |
| Maximum allowable indicated airspeed for undercarriage and flap extension | 200km/h | 108kts |
| Indicated stalling airspeed at braking with flying weight of 1570kg – 1620kg when the engine is at idling conditions Clean: Flap extended: Nominal I Clean: Take-off regime (gear down/flap): | 120-123km/h 112-114km/h 102-105km/h 97km/h | 64-66kts 60-61kts 55-56kts 52kts |

### Operational Loading

| At take-off weight of 1,500kg | +6.4 / -3.2 |
| --- | --- |
| At take-off weight of 1,650kg | +5 / -2.5 |

### Crosswind Components

| Maximum permissible headwind velocity at take-off and landing | 15m/s (29kts/33mph) |
| --- | --- |
| Maximum allowable crosswind speed at 90° runway angle at take-off | 12m/s (23kts/26mph) |
| Maximum allowable crosswind speed at 90° runway angle at landing | 10m/s (19kts/22mph) |
| Maximum allowable headwind speed when landing without the extended split flap | 10m/s (19kts/22mph) |

### Weight and Balance Data

|  | Versions |
| --- | --- |
|  | Trainer version | Initial training |
| Take-off Weight | 1,650kg (3,638lbs) | 1,510kg (3,329lbs) |
| Total load | 438kg (966lbs) | 303kg (668lbs) |
| Fuel | 100kg (220lbs) | 100kg (220lbs) |
| Equipment | 338kg (745lbs) | 203kg (447lbs) |
| Crew – including: |
| Pilot (1/2 persons) | 80kg (176lbs) | 185kg (408lbs) |
| Cadets (3 persons) | 240kg (529lbs) | - |
| Equipment without crew: |  |  |
| Seat cushions | 5 | - |
| Parachutes | - | 25 |
| Oil | 18 | 18 |
| Aircraft empty weight | 1,217kg (2,683lbs) | 1,217kg (2,683lbs) |
| Centre-of-gravity (c.g.) position, %MAC (mean aerodynamic chord) - At take-off, RG retracted - At landing, RG extended with 10% fuel and 50% oil - Empty, RG extended - Permissible CG position range, %MAC | 24.5 23.4 18.5 13.0-26.0 | 19.5 17.8 18.5 13.0-20.5 |

- Aircraft empty weight allowance is ±1%

- Empty aircraft c.g. position tolerance is ±1% (MAC – mean aerodynamic chord)

- The undercarriage extension displaces the centre-of-gravity forwards by 0.5%-0.7% MAC

- In the initial training version, the crew weight includes two parachutes C-4.  Assumed weight of the parachute is 12.5kg

- One of every five mass-production aircrafts feature the wiring and attachment fittings for the OSB-1 and PB-5 radio stations.  When these stations are installed, the mass of the aircraft becomes increased by 10kg and the CG position of the aircraft becomes displaced 0.5-0.6 %MAC aft ward.  The OSB-1 and PB-5 stations are installed only in the advanced training version aircrafts.  In this case the take-off mass of the empty aircraft is increased by 25kg.  The CG position of the aircraft shits 1.6-2.3 %MAC aft ward.  For aircrafts not equipped with SARPP-12K flight data recorder the mass of the aircraft decreases by 10kg and the CG position of the aircraft shits 0.3-0.5 %MAC forward.

### Other Limitations

- Due to the fact that the aircraft does not feature regular oxygen equipment, flights at altitudes more than 4,000m are prohibited

- In the trainer version, the number of the crewmembers should not exceed four persons

- As parachutes are not employed in the trainer version, it is PROHIBITED to make aerobatic manoeuvres.  However, in the initial training version with a crew of two persons equipped with emergency parachutes, all elementary and advanced manoeuvres can be performed

- Prolonged inverted flight and return (backward) flying is strictly PROHIBITED

- Night training flights from non-lighted runways is prohibited

- Take-off is prohibited if the quantity of available fuel is less than 60litres.  In the case of illumination of the RESERVE 30litres (Oct. 30l) light annunciator the aircraft is allowed to fly not more than 40-45mins.  Flights in the circuit should be performed with LG extended.  The minimum sub-soil strength for taxiways and runway is 4 kgf/cm²

## Section 4 - Pre-flight Inspection

A quick review of your logbook will make it obvious how long ago it was that you flew in a Yak 18T.  Whether you are the sole owner or a shareholder, you should always treat the aircraft with critical and suspect eyes.  Whether you were the last to fly just yesterday or not, always perform an unrushed formal pre-flight inspection.  The number of AAIB reports indicating inadequate pre-flights is unnecessary and avoidable.  It takes 15-30minutes to do a good pre-flight; the best advice is to know what to look for and CHECK PROPERLY.

The following suggested pre-flight inspection is targeted at the pilot who is travelling alone – hence the structure of the checks and the engine starting procedures.   The process of conducting the pre-flight inspection for those with willing and able assistance will no doubt be improved.  In any case, it is recommended that you take full responsibility for all of the checks, allocating only insignificant tasks to others until you are convinced of their competence.

### Preliminary Pre-Flight Actions

The following steps should be carried out prior to beginning the inspection, make sure that all covers and protective caps i.e. pitot cover, propeller cover, oil cooler stop, cockpit cover, aileron and rudder gust tabs are removed.

- at dusty aerodromes the parking area of the aircraft must be HOSED

- REMOVE any wing and tail tie-downs

- in winter make sure that the aircraft is CLEANED from snow, ice and frost

- if parked on grass, REMOVE any mud and grass from the undercarriage – also, check for unwanted items in the undercarriage recesses

- REMOVE any items (typically grass and hay) located in the oil-cooling unit at the front of the starboard wing near the cowling

- LEAVE the chocks under the main wheels and ensure that fire extinguishing aids are close to the aircraft in the event of a fire

- CHECK that there are no PEOPLE, SUBJECTS or VEHICLES NEARBY capable of obstructing the propeller

Ensure that all precautions are taken to prevent against spontaneous folding of the undercarriage, the engine occasional start, cut-in of individual electric units and extension of the split flap.  For this purpose check the following –

- SWITCH the BATTERY-GROUND SUPPLY to the OFF position

- ENSURE that all switches and cut-outs on the panel are switched OFF

- CHECK that the magneto switch is SET to 0 position OFF

- CHECK that the undercarriage lever is in the DOWN position and locked with a detent.  If no detent is available, advise all assistants and passengers of the importance not to touch this lever

- ENSURE that the flap lever is in the NEUTRAL position

- in winter time, check that the gills are CLOSED (remember to check visually that the gills are actually closed when you think they are)

- ENSURE that the oil cooler is CLOSED (remember to check visually that the oil cooler shutter is closed when you think it is)

- CHECK that the carburettor heat is OFF

While in the cockpit, it is advisable to do a quick instrument check of the fuel contents –

- SWITCH the BATTERY-GROUND SUPPLY to the ON position

- SWITCH the ENGINE INSTRUMENTS to the ON position

- NOTE the reading of BOTH tanks from the fuel contents gauge

- SELECT and hold the switch for the LEFT fuel tank contents and wait for the gauge to stabilise and note the reading

- SELECT and hold the switch for the RIGHT fuel tank contents and wait for the gauge to stabilise and note the reading

- COMPARE the individual readings with the total fuel contents and that of the expected contents (i.e. as stated in the engine log book)

- unless full-fuel is required, avoid deciding on this basis if the aircraft needs additional fuel until you have VISUALLY checked the contents of each tank, just in case the gauges are inaccurate

- SWITCH the circuit breaker ENGINE INSTRUMENTS to the OFF position

- SWITCH the circuit breaker BATTERY-GROUND SUPPLY to the OFF position

- if additional fuel is required then inform the ground staff now

- NOTE: all switches should be OFF

It is now advisable to perform a very quick check of the ANE (air navigation equipment).  To do this, perform the following actions and remember that battery power is limited and will not last long; a quick check is all that is necessary to ensure that the lighting facilities function correctly -

- SWITCH the BATTERY-GROUND SUPPLY to the ON position

- SWITCH the ANE switches to the ON position

- get out of the cockpit and CHECK the port side wing tip ANE light

- move around to the front of the aircraft and CHECK the landing/navigation light on the port wing

- while moving around to the starboard wing tip, CHECK the landing position lights on the front and main undercarriage

- CHECK the starboard side wing tip ANE light

- while moving to the rear, CHECK the anti-collision beacon

- while moving to the port side, CHECK the rear tail ANE and then enter the cockpit

- SWITCH the ANE switches to the OFF position

- SWITCH the BATTERY-GROUND SUPPLY to the OFF position

- NOTE: all switches should be OFF

### Relevant Documentation

Before the equipment is inspected, the pilot-in-command must look through the flight logbook to check whether any reported defects (detected during previous flights) have been eliminated.  It is important to get to know what kind of works/repairs have been performed on the aircraft by technical personnel.

If a group manages the aircraft then seek information about the maintenance schedule and if action needs taking – ACT!  From this point on, you the pilot-in-command become responsible for the readiness of the aircraft for flight -

CHECK!

### Performing the Inspection

###### Pre-flight Checks

Checking the Fuel and Oil

- The amount and grade of the available fuel and oil must be CHECKED and REPLENISHED if necessary. The pilot-in-command must be sure that the fuel deposit is discharged and is free of mechanical additives and water and in wintertime ice crystals

Checking the Oil

- The oil contents are checked by the means of a dip-yoke attached to the oil cap on top of the cowling.  First CHECK the oil by climbing on the starboard wing, edging forward avoiding the oil cooler until you can comfortably remove the oil filler cap without losing your footing.  If you are quite a heavy individual or are uncomfortable with this approach, find some step-ladders and climb from either side of the cowling – it’s safer this way

- REMOVE the cap, undo, remove and check the dip-yoke and ENSURE that the oil contents are in the range of 12-14litres for ordinary flight (>8litres for aerobatic flight).  The standard oil level reading is 18litres. The total oil tank volume is 30litres

- ADD the correct grade of oil as required by using a funnel being careful not to spill the oil during the process

- Once satisfied with the oil contents, ensure that you REPLACE the dip-yoke and cap correctly and SECURELY.  CHECK that the dip-yoke cap is held tight under the edges of the oil filler tab and then tighten

- When refitting the oil cap on top of the cowling, ENSURE that the cap is placed correctly and that the screw ‘clicks’ into place to fasten the cap correctly

- NOTE the quantity of oil and the amount added in the engine log book

Checking the Fuel Deposit

- To drain and INSPECT the fuel contents, move underneath the fuselage to identify the fuel drain cap (only 1 fuel drain on a Yak 18T).  This is located aft of the cowling, just in front of the split flap

- Carefully UNSCREW the locking screws and allow the fuel cap to open on its hinge.  Note, use the right tool and avoid using excessive force when opening the cap as this will decrease the life of the screw heads

- Use a reasonably large clear container (unlike the usual test-tube like drainers).  HOLD the container beneath the drain and PUSH the release valve to allow the fuel contents to fill the container

- CHECK that the fuel is free from mechanical admixtures, sediments, water, ice crystals and is of the correct colour (i.e. blue).  It is quite normal to drain 200ml-300ml of fuel

- If unsatisfied with the fuel contents, RE-DRAIN and RE-CHECK.  If you are in doubt, err on the side of caution and seek additional advice – do not rely on hope.  We all know that the carburettor can become blocked and hence stop the engine at a critical time

- REPLACE the fuel cap and as before, carefully lock the securing screws in place without using excessive force

Visual Fuel Inspection

- With a full tank reading, the fuel level in the tanks must be BELOW the edges of the tank fillers by at least 3cm.  The total capacity of the fuel tanks is 193litres (more for those 18T’s with extended wing or wing-tip tanks)

- REMOVE the fuel cap and fuel lock on the port wing (similar to when checking the oil)

- REMOVE the inner fuel filter and then use a fuel dip-yoke (if available, visually if not) to MEASURE the contents of the tank.  Note: with extended wing tanks, it is not possible to gain an accurate measure of the tank contents by visual inspection due to the wing dihedral

- REPLACE the fuel filter and lock and ensure it is correctly positioned and SECURE (similar to oil) even if you are awaiting additional fuel

- REPLACE the fuel cap and lock the screws in the correct position

Performing the Walk Around

- Perform the walk around SLOWLY; take your time.  If you are in a rush, then think about the implications of missing something vital and then ask yourself what is more important?  The diagram below suggests a route for the walk around.  By all means design your own, but whatever you decide, ensure that the walk around covers everything that is vital and once you have adopted a route, stick to it and improve it.  AVOID the complacent ‘quick-random-check’ syndrome.

Perform the external inspection of the aircraft with the following checks –

- CHECK that the air valve inside the port-side cowling has been released and that no air is present by opening the valve.  Do not over tighten this value

- CHECK the engine cowling to make sure that no damage is present and that the cowl fasteners and cover plates are shut and secured correctly (slits of the fasteners should coincide with marks on the cowling)

- CHECK the spinner/hub, ensure that all of the screws are secure, especially on either side of the propeller blades where they meet the spinner

- CHECK the propeller blades and the blade counterweights for stone chips on the reverse side and other damage and cracks

- CHECK propeller blade setting according to setting marks

- CHECK for leakage of petrol and oil

- CHECK the undercarriage and fixture of the undercarriage extension signal lights, be sure that the tyre casing of the nose undercarriage leg is not damaged, the tyre pressure is a standard one (15-20mm tyre deflection), the damper conditions is proper (no mixture leakage) and camber of the shock-absorber strut is normal, a visible portion of the stem should de equal to 173-187mm

- CHECK whether tyre casings of the main undercarriage legs, grounding springs and signal lights fixtures of the undercarriage lowering are proper, the tyre pressure is standard (25-30mm deflection) and the sag of the shock-absorber struts is equal, the visible portion of the stem should be 204-234mm

Main Undercarriage

| Example Undercarriage | Front Undercarriage |
| --- | --- |

- CHECK the centre-wing section from below

- unlike the diagram below, make sure that the landing split flap is raised and fits TIGHTLY and that no fuel or oil leakage is present

- CHECK the starboard wing and look for damage of the wing skin and fillets

- CHECK the state of the air intake, oil cooler and cells

- CHECK for oil leakage and the proper condition of the extended undercarriage position indicator and state and fastening of the position lights

- CHECK that the ailerons are good and joint couplings are proper, and that the clamps are taken off and the aileron can be freely deflected

- at ambient temperatures of less than -5°C, CHECK whether a shutter is installed on the radiator cells

- CHECK the starboard side of the fuselage, ensure that the cabin glazing, fuselage skin and radio station aerial are not damaged.  Also check that the security of attachment to the fuselage is proper

- CHECK along the top of the fuselage to the point where the tail fin joins the fuselage, looking for signs of stress and any disfiguration or panel movement

- INSPECT the tail unit for external defects

- ENSURE that the horizontal and vertical stabilisers and their fillets are free from mechanical damage

- CHECK that the hinge joints of the elevator and rudder are serviceable and are properly greased, see whether cramps are proper

- CHECK fastening of bracing struts, case of the elevator and rudder deflection

- CHECK the elevator trimmer is operational by winding it lock-to-lock and then SET it back to the NEUTRAL position.  It is possible for the elevator trimmer wire to come off of its spindle.  If you anticipate that this is the case during the winding, cease to test the trimmer as this will only make the corrective action more difficult

- CHECK that the flashing anti-collision beacon and tail position lights are not defective

- INSPECT the port side of the fuselage, CHECK its skin, see whether the locks of the luggage compartment and board hatches are closed, secure and fastened to the fuselage.  The luggage compartment lock is renowned for looking locked but not actually being locked – check this is not the case by firmly pushing the luggage compartment from the inside behind the rear seat

- CHECK the radio-altimeter aerial, radio compass and marker aerials are not damaged

- CHECK state of glazing, the cabin door and door hinges.  Water has been known to creep down into the slim cabin door pockets. If this is the case, remove the water before continuing

- CHECK the port wing, check the state of the wing skin and presence of fillets, condition of an aileron and joint couplings. See whether cramps are withdrawn and the fastening is proper

- INSPECT the state of pitot-static tube PST, see whether the pitot cover is removed and the undercarriage extended position indicator is sound and that the landing light is not damaged

The pilot should check the following prior to entering the cockpit -

- that the cockpit is FREE from foreign objects, the seats are INTACT and mechanisms of the door latches are PROPER. The door locks can become difficult to close properly RESOLVE before you get to the point of doing your power checks

- the state of the SAFETY HARNESSES and the mechanism of fitting the shoulder straps is secure and operational

- the presence of PARACHUTES in both front seat pans, checking that the parachutes have been repacked according to regulations (4 if carrying passengers, remembering weight and balance checks)

- the presence of LIFE-JACKETS in both front seat pans if crossing water (4 if carrying passengers)

- the presence of a LIFE-RAFT on the rear shelf or on an appropriate seat if crossing water

- CLEANLINESS and the condition of the glass cockpit windows being intact.  Clean both inside and outside if necessary

- if passengers are to be carried, the pilot may now allow them to the enter the cockpit, providing them with clear instructions as to what to do to install themselves and fasten the RESTRAINTS, LIFE-JACKETS and PARACHUTES where appropriate

- the pilot must then CHECK that all passenger restraints are correct and that no items are trapped outside when the cabin door when it is closed

- the pilot is now obliged to provide the first part of the pre-flight PASSENGER BRIEFING, giving the passengers plenty of time to understand and question the talking procedure, take-off, enroute and landing processes, exit procedures and priority and noises to expect.  If appropriate, ask one or more of your passengers some questions too and ask them to keep a good look out to the port or starboard side/s

After entering the cockpit, the pilot should proceed as follows –

- PUT feet on the rudder pedals under the pedal belts and, if necessary, ADJUST the seat so as to be able to fully deflect the rudder pedals and the yoke to their full extent

- CHECK to be sure of easy and positive action of the yokes and rudder pedals and of the correctness of the controls and ailerons for FULL AND FREE deflection

- CHECK whether the parachute spring hook is attached to the pull ring on the seat pan

- CHECK to ensure that the seat harness release is intact

- FASTEN waist and shoulder straps and press yourself to the seat back and tighten waist straps in the buckles. By means of a handle of the tightening mechanism retract and lock the shoulder straps and then tighten the buckles – ensure that you can still REACH all necessary instruments

- CONNECT the radio communications headsets

- CHECK whether the cockpit's doors are closed and properly clamped in the locked position with by the latch and the lock

- CHECK for the proper state of the flight and navigation instruments as well as other instruments, SET the altimeter pointer to zero and check whether the altimeter barometric pressure corresponds to the actual value at the aerodrome level pressure at a given moment (with a difference of not more than +1.5mm of Hg.)

- CHECK clock reading, wind it up and SET the correct time and reset the counter

Check the engine controls –

- CHECK the motion of the thrust lever from idle to fully open

- CHECK the action of the pitch control lever

- CHECK that the carburettor heat control lever can be easily moved (after checking stop heating by placing the lever fully upwards)

- CHECK the opening and closing of the cowling gills and radiator shutters, ENSURE that the control wiring does not jam and that the cowling gills and radiator shutters are closed and open when you expect them to be – CHECK VISUALLY: do not expect that everything is fine just because the control levers feel normal.  If the gills are not opening and closing freely, then it is possible to loosen the equipment by squirting aviation lubricant in the cowling joints on the front of the cowling, being careful not to disconnect the small springs connected to some of the gills

- ENSURE that the FUEL SHUT-OFF VALVE is pushed as far forward as it will go. i.e. fuel is not cut off

- Now OPEN the air system valve by turning it fully to the left and –

  - CHECK air pressure in the main and emergency cylinders which must be 50  ±5 kgf/m²

  - PROPER functioning of the landing split flap-operating mechanism (its extension and retraction) and CHECK the proper state of the warning light. To do this, move the flap lever to the position RETRACT (counter pressure is to be created) and then to the EXTEND position and control the flap extension by means of a red indicator FLAP EXTENSION on the panel which will LIGHT UP at this moment.  Then RETRACT the flap, to do it SET the flap lever to the position RETRACT and on making sure it has been retracted from a red indicator light FLAP EXTENSION which will go OUT on the panel, place the flap lever in the NEUTRAL position.

  - NOTE: if the air pressure is low, you may omit this step for now, until the engine is operational and the air pressure is being recharged

- CHECK air-tightness of the braking system, fully apply the brakes and ENSURE that no noise or hissing of air can be heard.  Leave the brakes in the ON position and continue the checks in the next section 5.1 Start Preparation

## Section 5 – Engine Start Preparation

The following text provides an overview of Hydraulic shock – if you have not read it before, you are urged to read it entirely before continuing.  If you have read it before, it is still worth reading it as a reminder.

### Hydraulic Lock/Shock Avoidance

This section kindly provided courtesy of Richard Goode Aerobatics (www.russianaeros.com)

The importance of preventing hydraulic lock can never be underestimated.  The consequences are at best expensive, at worst – catastrophic!  One fatal accident was caused by hydraulic lock, leading to total engine failure and a subsequent stall/spin.

### What is Hydraulic Lock/Shock?

In the normal functioning of the internal combustion engine, the piston moves towards the top of the combustion chamber.  (To avoid confusion we should realise that we are talking about the lower three cylinders on the M-14P, and therefore this is effectively at the bottom, at least in relation to the ground!)  If, however, a proportion of the combustion chamber is filled with a liquid – in this case oil, which is incompressible - something must give.  If the engine is turning with any degree of inertia – even being pushed through by the air-starter (although hand pulling cannot cause problems), the weakest part of the entire assembly is the connecting rod.

Thus, when we attempt to start an engine with oil in the bottom of the combustion chamber, and it certainly doesn’t need to be full, this will initially increase the compression and, at its extreme, simply results in the piston being unable to progress further, hence the connecting rod bending and shortening.

If you have any doubts about oil descending in these engines, you only have to see the amount of smoke following a start-up to realise that every engine has a fair amount of oil in the cylinders – but we of course are talking about more than that.  A fundamental cause is that the pistons are made from an aluminium alloy to a very high coefficient of expansion.  This means that, as it heats up, it expands to a much larger size and, in order to tolerate this, when cold it is quite significantly smaller than the piston bore, allowing oil in the engine to drain past the pistons, through the piston rings, and then down into the bottom three cylinders.

The other issue is that the M-14P has a dry sump, i.e. a separate oil tank, from which oil is sucked to feed the engine, and to which it is returned by the scavenge pump.  Normally a valve prevents oil from the tank, which is of course higher than the engine, descending into the engine unless the oil pump is turning.  However, this can become stuck, even by a small piece of dirt, and particularly over a period of time the entire contents of the oil tank can migrate into the engine and, inevitably, will end up in the lowest place – the lower cylinders.

### The Consequences

Once the connecting rod has bent, it is inevitable that it will ultimately break, although amazingly engines often continue to run with a bent connecting rod for a number of hours.  In the shorter term however, the bottom piston ring (of course, with inverted cylinders, the one furthest away from the ground), comes very close to the end of the cylinder at the bottom of its stroke, i.e. geographical top).  With a bent connecting rod it is quite likely that the final oil-control piston ring will jump out of the cylinder. Then of course, when the piston is forced back into the cylinder, the piston ring will break, which initially will lead to high oil consumption, and almost inevitably to pieces of the ring being found in the front oil-filter, with an indication also from the chips-in-oil.  If nothing is done at this stage, the connecting rod will break.

The consequences of this can be truly dramatic, in one case the main crankcase bolts shot forward not only through the gills (quite easily), but also right through the passing propeller blade!

It is also quite likely that mechanical mayhem on this scale could cause the engine to seize totally, and if this happens suddenly it will very likely tear itself out of the frame, with a consequent problem of a quite serious shift of C of G to the rear.

### What can be done?

The obvious answer is to not start the engine with oil in the bottom cylinders.  What one should realise, however, is that there is oil not only in the cylinders, but also in the three bottom intake-tubes.  An examination of the engine will show you that a tail-wheeled aircraft (e.g. Yak-50 or Sukhoi) will have a much higher tendency to collect oil in these tubes than a nose-wheeled aircraft.

For this reason those owners who think that merely by turning the propeller through 20 or whatever blades before starting, they are totally avoiding hydraulic lock are deluding themselves.  Certainly this will dislodge oil already in the cylinders, but it will do nothing to remove the oil in the intake tubes, which immediately after starting, is sucked into the engine, then possibly causing hydraulic lock.

For this reason the designers put drain plugs in the three bottom cylinders, as well as thoughtfully providing a special spanner with which to remove these plugs.  The problem with this is that it does take some time to remove the lower engine cowl and drain these intake tubes.  However, you ignore this at your peril.

Thus, for the original operators of these aircraft, as soon as an aircraft had not been used for a day or so, it was absolutely routine to undo the cowls and drain oil out of these intake tubes.  Few of us however have our trained mechanic to do this before flying, and all too often it is neglected.

A final way of minimising the problem is to ensure that every engine is run for at least 30 seconds at 60% before shutting down (remembering of course that the engine should not be shut down at above 1500 cylinder head temperature), which will scavenge excess oil from the engine into the oil tank, as well as get rid of oil in the supercharger, which is after all, the oil that ultimately drains into the intake tubes.

### Other Solutions

Given the reluctance of the average pilot in the West to spend more than a couple of minutes with an aircraft before flying, it is inevitable that people have been thinking of ways of banishing hydraulic lock.

| Sergio Dallan method | Sergio Dallan, an Italian Sukhoi owner and an exceptional engineer, pondered the problem at length, and his solution comes in two parts: i) A master oil-tap at the bottom of the oil tank, which is (thankfully) connected to a warning light and an external visual signal, whereby after flight the oil supply is switched off and therefore cannot drain out of the oil tank. Hopefully of course the oil is switched on again before starting. ii) A clear window on the gearbox inspection plate enabling the propeller to be turned after shutting down to the position whereby the crankshaft throw is in its highest position. In this way oil cannot drain through the crankshaft and then slowly leak out of the big-end bearings and then into the lower cylinders. The system is good, but is not cheap (US$1,000), as well as taking a day and a half to install, and the slight possibility arising of starting with the oil still switched off. |
| --- | --- |
| Manifold drains | The next obvious way of combating the problem is a system whereby pipes are attached in the three lower manifold drain plugs, which then either go to individual drains or, more commonly, collect together into one larger pipe, and then into a fuel-drain type tap, which is opened after flight - oil slowly trickles through it, and before flight it is shut. This is an excellent system, although most of the systems I have seen incorporate small-bore pipes, which certainly would not allow oil in sufficient quantities to pass through when cold. There is also the need to shut the drain tap before the next flight. |
| Vedeneyev System | Vedeneyev are of course the original designers of the engine, and they have developed an ingenious, and fully automatic system whereby, after shutdown, oil drains from the three lower intake tubes into a container fitted to the bottom of the engine, which, on start up, is sucked slowly into the supercharger, and then into the cylinders and burnt. This system has the advantage of being totally automatic, as well as providing extra lubrication around the engine during the critical start-up period. Prototypes of it are now flying successfully, and it is hoped that the system can be offered on a commercial basis within a few months. Again however it is not a simple modification and the existing oil sump, i.e. the large green part of the engine you see projecting from between the lower cylinders, needs to be removed and machined. |

### Conclusion

Check that the engine was previously run for at least 30 seconds at 60% before being shutting down.  Turn the engine thoroughly through before every start and notice any oil coming out of the exhausts – even if you have only left the aircraft for half an hour (being aware of the engine temperature before turning is important to avoid it starting by itself).  Drain the intake tubes if you have left the aircraft for more than a day, or fit one of the systems above which will drain them for you.  If you have failed to start the engine after the second attempt and engine priming was conducted, then pull through the propeller to remove any excess fuel from the cylinders.

## Section 6 – Engine Start

At ambient temperatures of +5°C or less, the engine must be warmed-up from an airfield heater, to a cylinder head temperature of at least 30°C.  In this case, it should be quite easy to turn the engine propeller through by hand.

If the ambient temperature is between +5°C-10°C and if the oil in the engine and oil system is diluted with petrol then the engine can be started having not been warmed-up.  The engine can either be started from the aircraft accumulator or from the airfield power source.

##### CAUTION

- DO NOT turn the propeller when the engine is hot i.e. > 100°C (lower to be safer)

- DO NOT fill petrol up above the amount specified, as it can wash oil off the cylinder walls and cause a score of the pistons or can be accumulated in the bottom cylinders and also contribute to a hydraulic shock

- DO NOT fill the petrol up through exhaust branch pipes and spark-plug ports

### Prior to Starting the Engine

- CHECK that the propeller pitch lever is placed in the FINE PITCH position

- SET the thrust lever to the position corresponding to 1/3rd of fully open equivalent to approx. 28-38% engine rpm

- ENSURE that the fuel cut-off valve is in the open position i.e. FULLY FORWARD

- at ambient temperatures below zero, SET the carburettor heat control lever (adjusts air getting into the carburettor) to the ON position (i.e. fully downwards)

### Avoiding Hydraulic Shock

- CHECK that the engine was shutdown using the correct procedure i.e. run at 60% for at least 30 seconds at the correct temperature setting – if not, it is advisable to drain the bottom three cylinders for hydraulic shock avoidance

- TURN the propeller through until the oil that may drip from the exhausts ceases completely.  This may take several revolutions

- Now WAIT for the oil to stop dripping completely and then turn the propeller through a few more times looking for signs of further oil expulsion from the cylinders and repeat if necessary

### Engine Priming

- TURN propeller (3-4 revolutions); during the propeller turning, SET the primer MOTOR PRIMING to the CYLINDER position and fill up 2-3 primers of petrol into the engine cylinders in summer and 3-5 primers in winter time.

- GOOD ADVICE, but this is a tad difficult if you are on your own!  Prime the cylinder, turn the propeller, prime the cylinder, turn the propeller, prime the cylinder and turn the propeller.  Laborious but necessary and “Yes”, you do need to get in and out of the cockpit each time.  Also, if you are on wet and muddy ground, you need to think about cabin cleanliness too

- Now SET the MOTOR PRIMING primer to the FUEL LINE position and GENERATE the fuel pressure in front of the carburettor to 0.2 to 0.5 kgf/cm²

- NOTE: this pressure will drop with time and may need to be restored prior to start – DO NOT over prime more than 0.5kgf/cm²

- upon completion, SET the primer back to the CYLINDER position ready to provide additional fuel into the cylinders upon starting (i.e. the primer should be pulled out)

### Engine Starting

To start the engine, the pilot should proceed as follows -

- have a good look round and check for any PEOPLE, ANIMALS or VEHICLES that may have unexpectedly approached the aircraft

- even if your aircraft does not have the small windows at the front of the cockpit, it is still advisable to open the cockpit door, look around and announce loudly “CLEAR OF PROPELLER” and listen carefully for any response

- once happy, close the cabin door and fit your safety harness securely

- SWITCH the BATTERY-GROUND SUPPLY to the ON position

- SWITCH the circuit breakers IGNITION, UNDERCARRIAGE WARNING, ENGINE INSTRUMENTS, ELECTRIC TURN INDICATOR and GYRO-HORIZON to the ON positions

- TURN the start button-casing counter clockwise until the red mark is pointing north.  The starter button is now live and the engine is now ready to be started

- LOOK AROUND AGAIN for any PEOPLE, ANIMALS or VEHICLES

- PRESS the START button as far as it will go.  Duration of a continuous depression should not exceed 3 seconds

- after the propeller has been turned through 3-5 turns, switch the MAGNETOS ON by setting the switch to 1+2 position.  To provide a more successful start of the engine after the first flashes, feed additional fuel into the cylinders with the help of the primer (which was intentionally left out in the previous steps)

- DURING start, if flashes appear in the cylinders, it is allowed to continue the engine starting procedure by displacing the thrust lever forwards and backwards in the range of revolutions, corresponding to 28%-60%, a throttle retard and accelerate rate is 2-3 seconds

- after STABLE ENGINE OPERATION has been obtained, RELEASE the start button and SET the thrust lever to the position corresponding to 38%-41%, while simultaneously observing the oil pressure and the pressure gauge readings

- after the engine start, LOCK the priming pump handle by setting it to the centre position.  MOVE the start button clockwise to the locked position, cut in the generator and warm-up the engine

- If the engine fails to be started after two attempts, stop the starting and identify the reason

##### CAUTION

- Prior to re-starting, observing all precautions (e.g. engine temperature) pull the propeller through manually by 4-8 full revolutions to remove fuel and oil from the cylinders which has remained there after a previous start (if it was performed with priming) in order to avoid hydraulic shock

- If during 15-20 seconds after the engine has been started, OIL PRESSURE does not reach a value of 1.0 kgf/cm2, SHUTDOWN the engine and find out the cause

Now that the engine has started, pay particular and frequent attention to the engine and oil temperatures and pressures and CHECK the following –

| that the undercarriage warning (three green indicators) lights come on, and check the proper state of red lights by pressing the test button |  |
| --- | --- |
| that the elevator trimmer control (when the trimmer is in the NEUTRAL position, a yellow/green indicator light TRIM NEUTRAL on the panel is ON |  |
| the state of electric instruments | (check whether the pointers are SET to their initial down positions) |
| the serviceability of the fuel level indicator, the total amount of fuel in the tanks and fuel amount in the left and right tanks separately note the amount of fuel that was added (if any) and compare against what is now indicated |  |
| the voltage of the airborne accumulator under load, to do it cut in the ANE (AHO) circuit breaker on the panel for 10-15 seconds, press the voltmeter button-voltage value should be at least 24V and is likely to stabilise at 27V-29V. The image obviously shows 0 |  |
| prepare and check the flight-control and navigation equipment and the radio instruments of the aircraft as well as the interior cabin lighting facility, if night flights are to be performed |  |

### Engine Warm-up

- Warm-up the engine at the crankshaft speeds of 41%-48% until the oil temperature at the engine inlet is increased. As fast as the oil temperature increases, accelerate the engine up to 44%-48% in summer and 51% in winter time and perform the engine warm-up at these conditions until temperature of at least 120°C of the cylinder heads is reached and the oil temperature not less than 40°C at the engine inlet is obtained

- The engine is considered to be warmed-up, if the temperature of the cylinder heads is not less than 120°C, the oil temperature across the engine inlet is not below 40°C and the temperature of air getting into the carburettor is not less than +10°C

- Once satisfied with the raising oil pressure and temperature, during the remaining period of the engine warm-up, proceed with the provision of the second half of your passenger BRIEFING

- After the engine has been warmed-up, ALTER the propeller PITCH by moving it twice from fine to coarse i.e. high to low

- With the help of the thrust lever DECELERATE the engine to minimum rpm

- CHECK again to ensure, that the cockpit doors are safely enclosed and locked with the catch

- UNLOCK the undercarriage lever by moving the latch to the left

- SET rudder pedals and the yoke to the NEUTRAL position

### Taxiing to the holding point

- REQUEST ATC taxi clearance to the hold.  Upon clearance, have a good LOOK around and RELEASE the brakes

After having received taxi-clearance, the pilot must proceed as follows –

- APPLY the brakes and accelerate the engine up to 64%-68%.  At this speed the aircraft should be HELD on the brakes and in position

- During taxi, perform the differential brake checks but do this SPARINGLY.  The braking system of the Yak 18T can OVERHEAT with a prolonged application of the braking mechanism, thus resulting in a complete brake failure on one or both sides of the system.  However, it must be noted that one can taxi reasonably well WITH MINIMUM BRAKE USE

- DECELERATE the engine to minimum rpm and ensure that no obstacles in the taxiing direction are present, release the brakes and accelerate the engine smoothly to the extent SUFFICIENT for the aircraft to start motion and proceed taxiing.  At night and if visibility is poor or reduced at day time, switch on lower beam and, if required, the upper beam of the land/taxi lamp

- Time of the land/taxi lamp switching-on should not exceed 5 minutes.  During taxiing, hold the yoke in the NEUTRAL position, use brakes smoothly and as short duration pulses.  Note: it may be necessary to deflect the yoke

- The speed of taxiing on a natural surfaced runway should not exceed 15km/h, on a concrete runway not more than 30km/h

- Perform taxiing at a slow speed, observing maximum care if the ground is slush-covered or rough, the terrain is unknown and obstacles are present nearby.  If taxiing on grass, beware that uneven ground can push the nose wheel into the air, sometimes quite high, so taxi at what you might think to be too slow a speed on all suspected uneven ground

- During taxiing at low engine crankshaft speeds, it is advisable to switch off the maximum number of the power consumers except for the radio station, flashing beacon and ANE and at night - to avoid discharging of the airborne accumulator due to prolonged taxiing which is not sufficient enough to charge the accumulator

### Engine Run-up

- Carry out the engine checks with the cowling gills and the radiator shutter CLOSED.  Prior to acceleration, SET the controls to the NEUTRAL position and BRAKE the wheels

- Run-up the engine to Nominal II, by pushing the throttle lever fully forwards and by increasing the propeller pitch simultaneously.  In so doing, the readings of the engine control instruments should be as follows –

| Crankshaft speed | 70% |
| --- | --- |
| Supercharger pressure (boost pressure) | Po+75±15mm of Hg |
| Oil pressure | 4-6 kgf/cm² |
| Petrol pressure | 0.2-0.5 kgf/cm² |
| Oil temperature at the engine inlet | 40-75°C |
| Cylinder head temperature | ≤ 190°C |
| Carburettor inlet air temperature | ≥ +10°C |

- The engine must run steadily and without shaking or abnormal vibration.  To avoid engine overheating as a result of insufficient airflow, the engine should NOT be operated continuously on the ground at the Nominal Rating conditions.

CHECK the correct functioning of the magnetos and spark plugs –

- SET the propeller to the FINE PITCH position

- USING the thrust lever SET a speed of 64%-70%

- SWITCH one magneto off for 15-20 seconds and compare the drop in rpm with the previous setting

- SWITCH both magnetos ON for 20-30 seconds (usually much quicker), until the initial speed is recovered

- SWITCH the second magneto OFF and compare the drop in rpm with the previous setting and note the difference in drops between both magneto checks

- SWITCH both magnetos ON

- The engine crankshaft speed (rpm) drop when one magneto is operating should not exceed 3%

- If the drop does exceed 3%, repeat the procedure until normal operation is achieved.  If after prolonged magneto tests a drop is still found to be more than 3%, one is advised to shutdown the engine and seek further advice

- APPLY carburettor heat and CHECK for a drop in engine rpm

CHECK the correct operation of the generator –

- SET the engine conditions to IDLING

- using the thrust lever SET the crankshaft speed to 57%-58%

- from extinguishing the GENERATOR FAILURE light, make sure that the generator has been connected to the aircraft electrical wiring system

- CHECK the voltage being produced by the aircraft through the electrical wiring system via the voltmeter by pushing the voltage check button, its reading must be 27V-29V

- SWITCH ON the power consumers required for the flight - converter, radio altimeter, radio compass, intercom system, VHF radio station, gyro-horizon inverted, compass system, gyro-horizon and the flashing beacon and for night flights, the air navigation equipment and the landing/taxi light

CHECK for the correct functioning of the propeller and rpm governor. To do this, proceed as follows –

- using the thrust lever SET a speed of 70% with the propeller's position SET to FINE PITCH

- SHIFT the propeller pitch lever to the COARSE PITCH position (fully backwards), in this case the crankshaft speed will be reduced to approximately 53%

- SHIFT the propeller pitch lever to the FINE PITCH position (fully forwards), the crankshaft speed will increase up to the initial value of 70%.  Notice a short-term oil pressure drop at the engine inlet.  Up to 2 kgf/cm² is allowed with a subsequent recovery during 8-11 seconds

CHECK for the correct operation of the propeller and rpm governor at the equilibrium speeds, for this purpose proceed as follows –

- using the thrust lever SET a speed of 70% with the propeller SET to a FINE PITCH position

- using the propeller pitch lever SET a speed of 64%

- by MOVING the thrust lever smoothly back and forth but not against the stop, make sure that the engine crankshaft speed remains UNCHANGED

- the engine speed can be increased or decreased by 2-4% respectively via an abrupt forwards and backwards motion of the thrust lever.  It’s equilibrium rpm will then be restored in 2-3 seconds.

CHECK the engine during 20-30 seconds. To do this, perform the following procedures –

- SET the propeller control lever to the position FINE PITCH forwards to the fine-pitch stop (decrease the propeller pitch completely)

- SHIFT the thrust lever smoothly forwards against the stop

The readings of the engine control instruments must be as follows –

| Crankshaft rational speed | 95%-99% |
| --- | --- |
| Supercharger pressure | Po+125±15mm of Hg |
| Petrol pressure | 0.2-0.5 kgf/cm² |
| Engine inlet oil temperature | 40°C-75°C |
| Oil pressure | 4-6 kgf/cm² |
| Cylinder head temperature | ≤ 220°C |
| Carburettor inlet air temperature | ≥ +10°C |

CHECK the engine running at minimum speed (rpm) with the propeller SET at fine pitch and the thrust lever SET fully backwards.  The engine should run steadily, the instruments readings must be as follows -

| Engine speed (rpm) | ≥ 26% |
| --- | --- |
| Oil pressure | ≥ 1.0 kgf/cm² |
| Petrol pressure | ≥ 0.15 kgf/cm² |

To prevent the spark plugs from getting FOULED, the duration of the engine running at minimum rpm should NOT EXCEED 5 minutes.  Also note that the low voltage generator light is expected to illuminate.

CHECK engine acceleration response.  For 2-3 seconds put the thrust lever smoothly from the idling stop fully forwards against the stop, in this case the propeller pitch lever must be in the position FINE PITCH.  Transition from the minimum speed (rpm) to the take-off regime should be performed smoothly during 3 seconds.  To provide the normal acceleration response, the temperature of the cylinder heads should be at least 120°C and the oil temperature at the engine inlet must be not less than 40°C

NOTE: the pilot can TEST of the engine acceleration response in flight.  This should be performed at an IAS of 160km/h

## Section 7 - Flying

### Take-off Preparation

Prior to requesting clearance for take-off, hold the aircraft with the brakes ON and carry out the following checks –

- CHECK the proper state of the gyro-horizon.  The aircraft is cleared for take-off only if the gyro-horizon is OPERATIONAL (i.e. actually operational for at least 3 minutes)

- CHECK that the compass reading CORRESPONDS to the take-off heading (when was the last time the compass was re-aligned?)

- CHECK that the landing split flap is RETRACTED

- CHECK propeller pitch is SET to the FINE PITCH position (i.e. fully forward)

- CHECK for full and free DEFLECTION of the yoke and rudder pedals

- CHECK elevator trim is NEUTRAL position (a yellow/green light TRIM NEUTRAL on the panel should be ON)

- CHECK that the cut-outs, switches and circuit breakers on the switch board required for the flying mission fulfilment are ON

- in case of possible carburettor icing or ice formation in winter, SWITCH the carburettor heat ON

LOOK around and on making sure that it is clear and that no unexpected aircraft are approaching, REQUEST a clearance for take-off.

### Take-off and Climb

Upon receiving the appropriate form of take-off clearance, enter the runway and TAXI along a straight line 3-5m in order to SET the nose wheel straight and over the take-off line, holding the brakes ON.

Immediately place the engine into the Nominal I regime.  Hold the aircraft with the brakes ON and check readings of the instruments controlling the engine operation.  The instrument readings must be as follows –

- cylinder head temperature 140°C-190°C

- recommended inlet engine oil temperature 50°C-65°C (at least 40°C and not over 75°C) and fuel pressure 0.2-0.5 kgf/cm²)

- oil pressure 4-6 kgf/cm²

- the engine must run without undue VIBRATION or SHAKING

- SWITCH ON the warning indicator DANGEROUS SPEED

On making sure that the engine OPERATES PROPERLY, CLEARANCE has been given and NO OBSTACLES are present on the runway, you may TAKE-OFF by selecting the engine TAKE-OFF regime

- SET the CLOCK to the ON position

- RELEASE the BRAKES and by a smooth moving of the thrust lever SET it to the take-off regime, i.e. fully forward

- DURING the take-off run, keep the yoke in the NEUTRAL position, compensate for the turns that may be necessary by gradually deflecting the rudder

- when the IAS has reached 80-90km/h, smoothly pull the yoke backwards in order to RAISE the nose wheel to the take-off position (10-15 cm off the ground) and hold this position until the aircraft rotates naturally upon the increase in airspeed.  NOTE: DO NOT raise the nose wheel too high.  The aircraft typically ROTATES as follows –

- with take-off weight 1,650kg IAS of 135km/h

- with take-off weight 1,500kg IAS of 125km/h

- what have you calculated it to be, given your load?

- After rotation, INCREASE IAS to 160-170km/h for a gradual climb.  NOTE: just after rotation, with the airspeed rising, the aircraft tends to quickly increase the pitch-up angle, be ready to COMPENSATE for this with the trim

- You may have been trained to take-off in a different way, i.e. as above, but upon rotation, level the nose to the horizon at about 30ft, with the undercarriage still down, so as to gain the maximum amount of airspeed without climbing and then to perform the climb out upon sufficient IAS.  If you HAVE been trained in this way then fine, if not, continue with the gradual climb approach.  Do not attempt this approach UNTIL you have received SUFFICIENT TYPE TRAINING. Also be aware that this approach may infringe your local circuit procedures so CHECK first

- At an altitude of at least 10m (~35ft) RETRACT the undercarriage. To do this, perform the following procedure –

- MOVE the undercarriage lever to the RETRACT/UP position, take care NOT to retard the lever to the NEUTRAL position

- CHECK that the undercarriage has RETRACTED by noting the illumination of the RED indicator lights on the undercarriage display panel

- CHECK that the undercarriage has RETRACTED by noting that the port wing, cowling and starboard wing undercarriage indicator SIGNALS have lowered into the airframe

- once SATISFIED that the lights and indicators are correct and that the undercarriage has been retracted, SET the undercarriage lever to the NEUTRAL position

By the time the undercarriage has been retracted and an altitude of ~300ft has been achieved, ALTER the engine conditions from the take-off regime to the Nominal I regime for the climb to circuit height –

- ACHIEVE a crankshaft rotational speed of 82%-84% by first reducing the propeller pitch and then by reducing the throttle to achieve the desired rpm.  This action is to be carried out swiftly

The climb is to be performed –

- at IAS of 170km/h at ambient temperatures up to +20°C

- at IAS of 180km/h at ambient temperatures over +20°C

- carry out the usual 500ft CHECKS

##### CAUTION

- CONTINUOUS engine running in the take-off regime is NOT to exceed 5 minutes

### Cross-Wind Take-Off

- The peculiar feature of this take-off is the necessity to DEFLECT the yoke into WIND since the very beginning of the take-off running

- This enables us to maintain a UNIFORM load on the main undercarriage wheels and to PREVENT banking during the take-off run

- A trend to the upwind turn should be COMPENSATED by sufficient rudder deflection

- As the speed increases and the aileron rolling power gets stronger, the yoke is gradually pulled to the NEUTRAL position so as to PREVENT the aircraft lifting on one wheel and placing undue stress on the other undercarriage leg

- When an IAS of 100km/h has been achieved, as above, by a smooth pulling of the yoke backwards, lift the front wheel to take-off position.  The crosswind take-off speed MUST be 5-10km/h HIGHER than that of a usual take-off

- The direction after rotation and while climbing is kept by following your PLANNED flight course

- NOTE: observe the cross-wind limitations of this aircraft

### Climbing

To prevent the engine from overheating, after you have achieved circuit height, perform the rest of the climb at the Nominal II regime with the engine SET at 70% and IAS at –

- 170km/h at ambient air temperature up to 20°C

- 180km/h at ambient air temperature over +20°C

While climbing -

- TAKE the load off the yoke by using the trimmer and check readings of the engine instruments

- CONSTANTLY observe the engine temperatures and that they fall within the recommended limits -

| Crankshaft rational speed | 70% (Nominal I) |
| --- | --- |
| Petrol pressure | 0.2-0.5 kgf/cm² |
| Engine inlet oil temperature | engine inlet oil temperature 50°C-65°C (maximum oil temperature 75°C, maximum allowable temperature during a long-term engine operation or not more than 15 minutes is 85°C) |
| Oil pressure | 4-6 kgf/cm² |
| Cylinder head temperature | cylinder head temperature 140°C-190°C (maximum cylinder head temperature during continuous engine operation is 220°C) |
| Carburettor inlet air temperature | ≥ +10°C |

Climbing from 3000m can be performed in the Nominal I regime with an IAS of 165km/h

### Engine Overheating (During the Climb)

If, while climbing, the temperature regime of the engine EXCEEDS the permissible limits with the cowling gills and the radiator shutters fully OPEN, the pilot should CEASE to climb, level out and increase the flight speed to REDUCE the severity of the engine conditions.

To DECELERATE the engine, first reduce the boost pressure using the thrust lever and then REDUCE the engine speed rpm using the propeller pitch lever.  If the measures taken do not result in the temperature reduction, the pilot should plan to END THE FLIGHT and INFORM ATC of the conditions and depending on the actual situation, land at the planned alternate airfield.

##### WARNINGS

- Deliberate flights into known icing conditions are PROHIBITED.  If the aircraft enters into an icing zone, the pilot must SWITCH on the CARBURETTOR HEATING, CABIN HEATING, CLOCK and change direction and/or the flight altitude

- Training flights into cloud are NOT allowed.  In the cases of inadvertent IMC, the pilot must level out by a smooth pulling of the yoke and continue to pilot the aircraft relying on the gyro-horizon and electrical turn indicator.  The pilot must compare the readings of the –

- gyro-horizon and electrical turn indicator and make sure that there is NO banking or turn

- gyro-horizon and the VSI indicator and make sure that the aircraft is flying HORIZONTALLY

The pilot should CONTINUE instrument flying and perform a 180° turn using a maximum 15° angle of bank and SET a descent of 2-3m/s to break out of the clouds

- Flying OVER 4000m can be performed only if OXYGEN equipment is available on board

### Horizontal Flight

When performing circuit flights (undercarriage up or down) it is advisable to maintain an IAS of 170-180km/h.  CHECK for normal engine running conditions during horizontal flight, these are the same for flight planning.

- After climbing to a specified level, SET the speed and engine boost pressure according to the engine regime selected.  At normal conditions during horizontal flight, the engine instruments should read as follows –

| Fuel pressure | 0.2-0.5 kgf/cm² |
| --- | --- |
| Engine inlet oil temperature | 50°C-65°C |
| Oil pressure | 4-6 kgf/cm² 1.0kgf/cm² at minimum rpm |
| Cylinder head temperature | 140°C-190°C |
| Carburettor inlet air temperature | ≥ +10°C |

- During warm weather, carburettor heat must be SWITCHED OFF as a high temperature of air coming into the carburettor causes a DECREASE in the engine POWER and therefore engine efficiency

- In all cases of horizontal flight in conditions of increased humidity with the air temperature becoming lower than +10°C, carburettor heating must be SWITCHED ON

- In-flight fuel consumption is to be monitored by using the fuel level indicators for both tanks and the clock.  When the RESIDUAL FUEL red light on the panel is illuminated, it means that 30litres of fuel remains in the tanks, this amount will be sufficient for a MAXIMUM OF 40-45 minutes of flying.

- Aircraft onwards of No.0604 have an improved emergency fuel capacity monitoring system that provides a separate remaining fuel warning in the main fuel tanks.  When the remaining fuel reaches 15litres, the fuel quantity low warning lights come on FUEL RIGHT or FUEL LEFT

- Controlled changes to in-flight engine power is recommended as followings -

a) to reduce power (conditions) -

- DECREASE the boost pressure

- DECREASE the engine crankshaft rotational speed to the specified one

- ADJUST the boost pressure

b) to increase power (conditions) –

- INCREASE the engine speed rpm to the specified one

- INCREASE the boost pressure

To AVOID oil thickening in the propeller hub cylinder during prolonged flight in steady conditions with low ambient air temperatures, it is necessary to shift the propeller pitch from a fine pitch to a coarse one at regular intervals (i.e. every 25-30 minutes) using the propeller pitch lever, changing the engine rpm within the 55%-67% limits.

One can monitor the correct operation of the Generator by checking the GENERATURE FAILURE red light on the annunciator panel or by using the voltage level tester on the voltmeter gauge.

### Chips in Oil

In flight, if the CHIPS IN OIL red light illuminates on the annunciator panel, the pilot is obliged to END THE FLIGHT IMMEDIATELY and to INTENSIFY control of the aircraft.

SPECIAL attention should be paid to the oil pressure and temperature at the engine inlet.  If the pressure drops or the oil temperature rises, INFORM ATC about it and land at the nearest aerodrome or on the nearest emergency landing ground.

It is PROHIBITED to perform any flight if the CHIPS IN ENGINE red light is illuminated before take-off.  This problem must be eliminated before flight.

## Section 8 – Aerobatic Flight Manoeuvres

The Yak 18T with M-14P can perform the following aerobatic and elementary flight manoeuvres.  The crew will determine the flight plan and altitude for aerobatics in each specific case.

- Aircraft weight for aerobatics should not exceed 1,500kg, the number of crewmembers must not be more than 2 persons.

- While piloting, manoeuvre recovery must be terminated at a level not lower than 1000m.  While performing aerobatics the g-load should not purposely exceed +3.5g to +4g.

- Prior to performing any elementary and advanced flying, trim the aircraft to an IAS of 180km/h and SET the engine crankshaft speed of 70%, i.e. Nominal II engine regime

- Perform a FULL CHECK of the engine instruments

- To PREVENT against the engine intolerable spin-up while performing elementary and advanced flying, do not exceed the speed over 300km/h (see aircraft flying limitations)

- It is PROHIBITED to perform any aerobatic manoeuvre without the appropriate type-training

This aircraft is cleared to perform the following aerobatic manoeuvres –

- Steep turns: 45° and 60° of bank

- Figure Eight

- Combat Turn

- Diving

- Steep Climb/Zoom

- Spiral

- Slipping

- Barrel/Slow Roll

- Flick/Snap Roll

- Normal 360° loop

- Half-loop

- Half-roll

- Spins

### Steep Turn: 45° of bank

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- Prior to entry into the 45° banked turn, SET the engine conditions to 70% and an IAS of 180km/h

- Then by a SMOOTH combined moving of the yoke and rudder pedals, put the aircraft into the banked turn.  The angle of bank is specified by the nose-over position and the front portions of the aircraft canopy relative to the horizon.  This position must be measured and controlled using the gyro-horizon

- The aircraft's entry into the steep banked turn is performed in the same way as the shallow turn.  As the bank develops, gradually INCREASE the boost to stabilise and maintain the 45° bank

- When the specified bank and required angular velocity is achieved, MAINTAIN the bank by slightly deflecting the yoke to the side opposite to the turn and forwards, simultaneously

- By pulling the yoke counter-clockwise and by deflecting the rudder pedals, eliminate the tendency for the aircraft to increase its rotational speed WITHOUT performing any side slipping

- CHECK the correctness of the turn by using the slip indicator ball and the electrical turn indicator

- 25°-30° prior to the specified ground reference point, begin the roll-out via a combined movement of the rudder pedals and the yoke in the opposite direction of the aircraft rotation

- Complete the turn recovery by slightly pushing the yoke forwards.  When the aircraft stops its rotation and is pulled out of the roll, SET the yoke to the NEUTRAL position and recover straight and level flight

- The aircraft should be STABLE throughout the entire process of the steep turn and the pilot should be able to easily shift from one direction of steep turn to another

### Steep Turn: 60° of bank

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- Prior to entry into the 60° banked turn, SET the engine conditions to 70% and an IAS of 200km/h

- Then by a SMOOTH combined movement of the yoke and rudder pedals, put the aircraft into the banked turn.  The angle of bank is specified by the nose-over position and the front portions of the aircraft canopy relative to the horizon.  This position must be measured and controlled using the gyro-horizon

- The aircraft's entry into the steep banked turn is performed in the same way as the shallow turn.  As the bank increases, gradually enlarge the boost so as to provide it to a full extent at a bank of 45°-50°.  When the 45° bank has been achieved and it continues to increase, pull the yoke slightly backwards and relax bearing against the rudder pedal, which has been deflected at the turn entry

- At a bank of 60° using proportional and coordinated pulling of the yoke and the rudder pedals, hold the aircraft in the turn.  Using the yoke, maintain the rate of rotation and the bank using the rudder pedals to retain the normal position of the nose-over relative to the horizon.

- When the specified bank and required angular velocity is achieved, MAINTAIN the bank by slightly deflecting the yoke to the side opposite to the turn and forwards, simultaneously

- By pulling the yoke counter-clockwise and by deflecting the rudder pedals, eliminate the tendency for the aircraft to increase its rotational speed WITHOUT performing any side slipping

- CHECK the correctness of the turn by using the slip indicator ball and the electrical turn indicator

- In the course of the banked turn, pulling of the yoke backwards is not allowed because during such a pulling a slight shaking of the aircraft makes its appearance, when the yoke is pushed forwards the vibration comes to an end.

- The turn recovery should be initiated 30°-35° before the specified ground reference point by using coordinated motions of the yoke and pedals, deflecting them to the side opposite to the aircraft rotation, in so doing, move the yoke forward simultaneously

- Complete the turn recovery by slightly pushing the yoke forwards.  When the aircraft stops its rotation and is pulled out of the roll, SET the yoke to the NEUTRAL position and recover straight and level flight

- The aircraft should be STABLE throughout the entire process of the steep turn and the pilot should be able to easily shift from one direction of steep turn to another

### Figure Eight

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- A figure eight is clearly a combination of two steep 360° turns in the opposite directions combined by a fast transition turn on crosswind leg to downwind leg

- It can be performed quite easily by following the procedure for the 45° or 60° steep turn.  However, during the reversal procedure it is necessary to push the yoke slightly in order to hold the speed

- As the banking lessens at the first 360° turn recovery, the engine boost should be decreased to 480-500mm of Hg and at the entry into the second 360° turn, the boost becomes complete

- Performing the figure eight manoeuvre requires special attention and a very exact motion and co-ordination of the control surfaces

- Complete the figure eight manoeuvre recovery by slightly pushing the yoke forwards.  When the aircraft stops its rotation and is pulled out of the roll, SET the yoke to the NEUTRAL position and recover straight and level flight

- The aircraft should be STABLE throughout the entire process of the manoeuvre and the pilot should be able to easily shift from one direction of steep turn to another

- A figure eight can be performed at either 45° with an IAS of 180km/h or at 60° with an IAS of 200km/h.

### Combat Turn

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space above the aircraft

- SET the rpm to 70%, provide a full boost and at a low speed decay increase the IAS to 280km/h

- Then by a SMOOTH pulling of the yoke backwards, approach the nose-over to the horizon line

- Using a fast and coordinated moving of the yoke backwards and to the combat turn's side at a simultaneous motion of the rudder pedals in the same direction, perform the aircraft transition to spiral climb with the initial bank of 15° to 20° and acceleration of 3.5-4

- A rate of entry into chandelle must be such that after a 130° turn the aircraft has a bank and a 50° climb angle, and with a further turn this position should be held

- On having made a 150° turn (30° before recovery reference point) by simultaneous moving of the yoke and rudder pedals towards the side opposite the turn, recover the aircraft so that the airspeed indicator reading at recovery is at least 150km/h, simultaneously, by a slight deflecting of the yoke forwards, provide a nose-over position relative to the horizon just the same as at the horizontal flight

### Diving

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space under the aircraft

- Perform entry into the dive from horizontal flight or from a turn at an IAS of 150km/h allowing NO NEGATIVE load factors

- Diving can be performed with the throttle open or closed with an IAS of NOT more than 300km/h at the recovery termination

- While diving, observe the engine temperature not allowing the temperature of the cylinder heads to drop BELOW 120°C

- The aircraft is to be recovered from a dive by a smooth pulling of the yoke backward

- Warning, the pilot will experience considerable g-loads with a fast pulling of the yoke at high diving speeds

- To PREVENT the IAS exceeding 300km/h during the dive recovery, the dive recovery should be started with 40°-50° descent angles with an IAS not more than 280km/h

### Steep Climb/Zoom

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space above the aircraft

- The steep climb/zoom is performed with a climb ANGLE up to 50°

- Prior to entry into zoom, SET the engine crankshaft speed of 70% (2050 rpm), provide a full boost and with a small descent increase the airspeed indicator reading up to 280km/h

- Specify a value of the climb angle, fix it and roll from the position of the horizon using the gyro-horizon instrument

- Proceed with recovery at the IAS of 170km/hr.  For this purpose, by means of a simultaneous rolling into a turn and decreasing climb angle at a constant boost, level the aircraft out

- The levelling out must be terminated at airspeed indicator reading of 140km/h

### Spiral

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space under the aircraft

- Perform the spiral from the steady state glide conditions at IAS of 180km/h with a 45° roll at the engine IDLING conditions or under the conditions, providing the vertical descent velocity of 3-4 m/s

- BEFORE entry into the spiral, CHECK the engine instruments and having SET the designated gliding speed using coordinated motions of the yoke and pedals, roll into a turn

- When the specified roll has been achieved by slight motions of the rudder pedals and the yoke towards the side opposite to the turn, ELIMINATE the tendency of the aircraft to increase its roll by increasing the angular rotational velocity and trajectory speed

- HOLD the bank value according to the nose-over position and the canopy nose sections relative to the horizon, control it by the turn and slip indicator and by the gyro-horizon instrument

- The pilots ATTENTION during the spiral must be distributed in the same way as during steep turns

- Temperature drop of the cylinder heads below 120°C is not allowed.  After spiral recovery SET the glide speed of 170km/h

### Slipping

- Slipping with retracted and extended flap is performed at an IAS of 170km/h

- Prior to slipping, select a ground reference point for direction-keeping, SET up a glide at the IAS of 170km/h

- Turn the aircraft away from the reference point by 10°-15° and by a smooth moving of the yoke create a BANK up to 20° towards slipping, holding the aircraft from a turn using the rudder pedal deflection to the side opposite to the roll

- While slipping, keep the flight direction using a reference point orientation, check the speed and keep it according to the nose-over position relative to the horizon and by using the speed indicator

- CHECK the designated bank by the aircraft inclination relative to the horizon and by the attitude indicator (gyro-horizon)

- RECOVER the aircraft from slipping by a simultaneous motion of the yoke towards the side opposite to the bank and slightly forward

- When the bank has decreased, place the rudder pedals in the NEUTRAL position and maintain a gliding speed of 170km/h

- Dampen the residual aircraft DRIFT after slipping with a return bank.  Do NOT allow the temperature of the cylinder heads to drop below 120°C while slipping

### Slow/Barrel Rolls

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- To perform a slow controllable roll, SET the indicated airspeed of 230km/h, the engine crankshaft speed equal to 70% with a full boost

- Then impart a pitch-up angle of 10°-15° and hold this position

- INITIATE a longitudinal rotation by smoothly deflecting the yoke in the direction of the roll.  When 45°-50° of bank has been achieved, proceed to pull the yoke being careful not to slow the rotation.  This is necessary to PREVENT the aircraft from turning when upside-down and to PREVENT the nose from dropping below the horizon

- After having PASSED the inverted position, with an angle of bank of 40°-50° before levelling out in order to hold the aircraft relative to the horizon.  INCREASE depression on the rudder pedal for rotation and as the aircraft approaches the 20°-30° banked attitude, hold the aircraft nose-over position within the horizon line by pulling the yoke backwards

- As soon as the aircraft approaches level flying attitude, STOP the rotation, SET the controls to recovery and then to the NEUTRAL position when rotation comes to an end.  The aircraft X-rotation/roll should be a UNIFORM one

- Good rolls should be performed WITHOUT altitude loss.  The procedure of making left and right rolls is the SAME

### Flick/Snap Rolls

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- To perform a flick roll, SET the indicated airspeed of 190km/h rpm 70% and the engine boost 650-700mm of Hg.

- Impart a pitch-up angle of 10°-15° to the aircraft and hold this position

- Then by means of a fast pedal deviation by 1/3rd of its motion towards the roll to be performed and by a slight pulling of the yoke and simultaneously deflecting it towards the deviated pedal, impart rolling to the aircraft

- The position the controls and the engine control lever is not changed during X-rotation/roll

- 20°-30° before the aircraft levelling out, SET the controls for recovery

- After the RECOVERY to level attitude, SET the controls to the NEUTRAL position.  The aircraft X-rotation/roll should be a UNIFORM one

- Rolls are performed actually WITHOUT altitude loss.  The procedure of making left and right rolls is the SAME

### Half-roll

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre

- Entry into a half-roll is carried out from horizontal flight at an IAS of 160km/h

- PRODUCE a pitch-up angle of 10° to 15° and then by simultaneous motions of the yoke and rudder pedals towards the desired half-roll, impart a ROTATION to the aircraft about an axis with such a rate that the aircraft will be turned upside-down in 2-3 seconds

- When the given position has been achieved, PLACE the rudder pedals in the NEUTRAL position and by using the yoke STOP the aircraft rotation

- REMOVE boost and by a smooth pulling of the yoke backwards make the aircraft go into a dive

- On achieving an IAS of 190-200km/h, gradually recover from the dive in such way that the IAS is 240-250km/h at the end of the dive recovery

- When performing the dive recovery, abrupt motions and excessive pulling of the yoke are NOT allowed as considerable g-loads will be produced

### Normal Loop

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space under the aircraft

- Using full engine boost and a small descent, accelerate to an IAS of 280km/h prior to loop entry

- With a SMOOTH pulling of the yoke backwards, proceed to making a normal loop with a g-load of +3.5 to +4g

- To PREVENT bank and turn caused by gyroscopic effects and yoke reaction torque, HOLD the aircraft firm using the left rudder pedal

- When the angle of climb is increased by more than 20°-30°, gradually INCREASE the rate of the yoke motion until the aircraft starts its transition to the upside-down position

- After this, REDUCE the pulling (pull forces) of the yoke.  At the top-most point of the normal loop, the yoke is pulled SLIGHTLY just so as to provide nose-down pitching

- If signs of aircraft INSTABLITY are present at the top-most point of the loop, move the yoke slightly FORWARD with a subsequent pulling BACKWARDS to create the required stabilisation effect

- As soon as the aircraft passes the line of horizon, smoothly reduce the boost to the minimum value

- WEAKEN the depression exerted on the left rudder pedal and feel the aircraft's “pushing” over

- When the VERTICAL dive position is achieved, slightly PUSH the yoke forward in order to provide a smooth dive recovery WITHOUT an abrupt transition to large angles of attack

- When the diving IAS is 190-200km/h, initiate the recovery to level flight in such a way as to obtain an IAS of 270-280km/h

### Half-Loop and Half-Roll

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space under the aircraft

- PRIOR to commencing this manoeuvre, achieve HORIZONTAL flight and select the intended recovery ground reference point

- Perform acceleration with full engine boost and a small descent.  The initial indicated airspeed of the half-loop is 300km/h

- When the designated speed has been ACHIEVED, perform the first half loop by pulling the yoke backwards more vigorously (i.e. with a g-load of +5g) than in the case of an inside loop

- Continue with the pull until a vertical angle of 60° has been achieved, then lower the g-load to about +3-4g

- On approaching the top point, with the aircraft in the inverted position and its nose-over does not reach the horizon line by 5°-10° (the IAS must be at least 150km/h)

- Now DEFLECT the yoke and rudder pedal towards the desired side, turn the aircraft about its longitudinal axis by 180° to perform the half-roll

- SET the controls for recovery at 20°-30° before recovering to level flight

- As soon as the aircraft's LEVEL attitude is achieved, SET the controls to the NEUTRAL position

- The IAS during the half-loop recovery must be 140km/h.  If the speed at the time of the half-roll is NOT 140km/h, then the half-roll is NOT ALLOWED to be performed.  TERMINATE the manoeuvre WITHOUT making the second half-loop

### Aircraft Behaviour at Large Angles of Attack and Stall

- Pilots are warned about the fact that the aircraft is approaching a STALL by an AUDIBLE signal in the headset and LIGHT signals (indication DANGEROUS SPEED on the annunciator panel) approximately 15 SECONDS prior to the stall

- The character of the Yak 18T can be remarkably DIFFERENT to that of a C172.  For example, a C172 experiences a relatively sharp nose drop after the stall has occurred.  The 18T has been known to produce a negative VSI upon stall without any other visible or audible signals so DO NOT RELY on receiving a stall signal for the awareness of the aircraft stall.  A good instrument SCAN and attitudinal awareness will help to highlight an imminent stall and UNEXPECTED negative VSI reading

- The warning detector is SET to the response indicated speed of 130km/h.  The warning indicator is cut-in by a toggle switch on the switchboard

- The aircraft controls retain their operational effectiveness at low flight speeds, up to the POINT of the actual stall

- Other symptoms at the point of stall include a nose down attitude with rolling either to the left or to the right side and a small shaking or buffeting

- By pushing the yoke FORWARD, the aircraft attitude will transition from the angle of incidence to one that is below the stall, but only once the speed INCREASES

- The indicated stalling speeds with ny=1.0 are as follows –

- in the cruise configuration at the engine conditions IDLING 120-123km/h

- in the cruise configuration at the engine conditions NOMINAL I 102-105km/h

- in the landing configuration at the engine conditions IDLING 112-114km/h

- in the landing configuration at the engine conditions TAKE-OFF 97km/h

- Large speed values correspond to the aircraft's weight of 1,650 kg, small ones to the aircraft's weight of 1,500kg

- At NOMINAL I engine conditions, with a full pulling of the yoke after the stall, the aircraft will ROLL either to the left or to the right with a greater VIGOUR than at IDLING conditions

- During 360° banked turns and spirals, while pulling the yoke BACKWARDS, the aircraft vigorously DROPS the nose with a simultaneous rising of the IAS an INCREASE in roll will also take place

- An even greater INCREASE will occur if dropping the nose at the time of stall, and more so, the higher the speed during the turn-spiral.  In moving the yoke FORWARD, the aircraft makes a quick transition to a sub-critical angle-of-attack

- In this case, pre-stall warning of shaking or buffeting is NOT felt.   However, at the time of the actual stall, a slight shaking or buffeting APPEARS

- The turn-spiral stalls with different engine conditions and c.g. positions DO NOT differ in their nature

- Given the right conditions when entering the stall, the 18T can be remarkably uneventful with the pilot noticing just an unexpectedly high negative VSI

## Section 9 - Spins

Spins are PROHIBITED unless the pilot has received appropriate spin training on type.  After such training and for continued training purposes, spins comprising of not more than TWO TURNS at a level of at least 3000m may be performed -

- BEFORE entry into this manoeuvre, study the surrounding airspace to make sure that no other aircraft are flying in proximity of your aircraft, that you will remain clear of cloud, congested areas and that sufficient altitude is available should the manoeuvre is not successful.  Select the necessary ground reference points for completing the manoeuvre.  Special attention should be paid to the space under the aircraft

- With the aircraft in level flight with an IAS of 170km/h and the crankshaft speed at 70%, balance the aircraft using the elevator trimmer

- Select a ground REFERENCE point for recovery from the spin

- CHECK that the engine instruments read as follows –

| Fuel pressure | 0.2-0.5 kgf/cm² |
| --- | --- |
| Engine inlet oil temperature | 50°C-65°C |
| Oil pressure | 4-6 kgf/cm² 1.0kgf/cm² at minimum rpm |
| Cylinder head temperature | 180°C-190°C |
| Carburettor inlet air temperature | ≥ +10°C |

### Entry into spin

Entering into a spin at LEVEL flight conditions –

- FULLY remove the boost and smoothly pull the yoke backwards as the speed decreases.  This will establish a pancaking regime.  Now CONTROL the aircraft to stop a wing from dropping or stalling -

- Entering a spin with the engine conditions higher than IDLING is PROHIBITED

- Increasing rpm in a spin is also PROHIBITED

- When entering a spin, pay particular ATTENTION to –

- the nose-over position relative to the horizon

- the reading of the speed indicator

- the readings of the variometer

- When the IAS of 125-120km/h has been achieved, DEFLECT the rudder pedal fully towards the specified spin direction and as soon as the aircraft initiates a wing stall and starts to drop the nose, apply FULL back yoke. Motions of the controls when going into a spin must be SMOOTH.  Entry into left and right spins is EQUAL

- During the spin, HOLD the controls in the positions that were used for the entry.  The character of the spin must consist of a uniform rotation; the spinning is vigorous but performed WITHOUT shaking or jerks

- The aircraft spins with an angle of the longitudinal inclination to the horizon equal to 50°-60° at the first turn, and 45°-50° at the second one

- At the first 3-tum spins the angle of longitudinal inclination is gradually DECREASED and angular rotational velocity rises at a constant speed and acceleration (ny=2).  After 3-4 turns the aircraft spin becomes STABLE with slight rolling oscillations, constant speed and acceleration

- At the first 3 turns there is no actual DIFFERENCE between the left and the right spins.  After 3-4 turns the RIGHT SPIN IS MORE sloping than the left.  Rotation during both spins is accompanied with some aircraft stalling VIBRATION or BUFFETING

- While spinning, direct a glance towards the spin direction by 25°-30° from the air aircraft X-axis and by 20°-30° below horizon

### Spin Recovery

To recover the aircraft from a spin, first –

- DEFLECT the rudder pedal towards the side opposite to the spin direction and after this in 2 seconds move the yoke forward beyond a NEUTRAL position by ¼-1/5th of motion

- NOTE: moving the yoke fully forward is not advisable, as this can result in dive angle increase, appearance of a negative load factor, rising of the indicated airspeeds and a LOSS OF HEIGHT during recovery

- As soon as the aircraft stops its rotation, immediately place the rudder pedals in the NEUTRAL position, increase the IAS to 160-170km/hr and then by SMOOTHLY pulling the yoke backwards, recover the aircraft from the dive at such a rate that the IAS reading at the end of recovery is 220-240km/h

- When the aircraft APPROACHES the horizon, increase the engine boost

- During three turns of the spin the aircraft's HEIGHT LOSS in recovery is 740m (approx. 2,400ft)

- The aircraft recovers from a spin (up to three turns) with a LAG not exceeding ONE TURN

- When recovering from a spin, always DEFLECT the rudder pedal AGAINST the spin EARLIER than the elevator.  In case of the REVERSE sequence the aircraft can FAIL to recover

- DEFLECTION of ailerons within up to ½ pro-spin motion does NOT affect the spin nature.  At a full pro-spin deflection the spin gets less stable and steeper; DEFLECTION of the ailerons by ½ of motion and fully against the spin, the latter becomes more FLAT in its nature

- Influence of the AILERONS on the spin nature is felt MORE at the RIGHT spin than at the left one

- While spinning, if the ailerons are DEFLECTED against the spin by MISTAKE and the aircraft FAILS to recover in two turns of lagging (after pulling the controls for recovery), proceed as follows -

- apply pro-spin controls (at the right spin the rudder is fully to the right side, the yoke is pulled fully backwards, ailerons in the NEUTRAL position) check to insure that they are in NEUTRAL

- make one turn with the pro-spin controls

- for getting the aircraft out of the spin, DEFLECT the rudder vigorously and FULLY against the spin and in 3 seconds after the rudder kick, move the yoke fully FORWARD.  A LAG, when this is done, can be equal to 1-1.5 turn at the left spin and 2-2.5 turns at the right one (The LAG during spin recovery is counted from the moment the elevator is applied)

- the aircraft recovers in a dive that is almost vertical when the rotation comes to an end, SET pedals to the NEUTRAL position and at acceleration of 3-4 recover the aircraft from a dive not allowing the IAS to exceed by more than 300km/h

### Recovery from an Inverted Spin

The Yak 18T is PROHIBITED from inverted spin training and practice flights.

- The aircraft's inverted spin is STEEPER than the normal spin.  It is NOT DIFFICULT to RECOVER

- This is done with a full and vigorous rudder pedal DEFLECTION towards the side OPPOSITE to the spin direction

- With a subsequent 1-2 second DELAY, deviate the yoke BACKWARDS beyond the NEUTRAL position (by ¼-1/5th motion).  The LAG experienced during recovery from the inverted spin is at LEAST 1 turn

### Unintentional Snap or Fall into Spin

The spontaneous fall into a spin can ONLY occur as a result of GROSS PILOTING ERRORS.

While training or in flying practice it is PROHIBITED to perform a fall into a spin from VERTICAL manoeuvres (i.e. zoom, loop, half-loop and combat turn).

Inadvertent entry into a spin from a 360° turn or spiral towards the side opposite to the bank is PROHIBITED.

- A spin CAN occur when making steep climbs, loops, half-loops and combat turns; usually when the yoke is pulled backwards and simultaneously the rudder (pedal) is fully deflected aside.  With the controls in such as position the aircraft first rolls and then drops the nose and goes into a spin

- In ALL cases of a spontaneous fall into a spin, REMOVE the boost IMMEDIATELY

- SET the aileron to the NEUTRAL position and determine the spin direction

- RECOVER the aircraft from the spin by using one of the methods mentioned above

- During training, to teach manoeuvring in order to CORRECT “errors”, an inadvertent entry into a spin is ALLOWED only from a descent turn (spiral) with the engine fully UNBOOSTED.  To perform an inadvertent entry into the descent turn spin –

- when the IAS is 150-170km/h the aircraft is rolled into 50-60° banked turn

- during the turn, PULL the yoke backward and simultaneously FULLY deflect the rudder pedal (against the stop) TOWARDS the turn

- the aircraft will vigorously ENTER into the spin

- after the second turn its spinning will be the same as during the spin entry at a minimum speed

- inadvertent entry into a spin from a 360° turn or spiral can be performed at levels of at least 3000m

- if the aircraft does not enter the spin but instead, makes a transition to an unstable deep spiral with a massive speeding up – it likely due to a pulling of the yoke and either movement of the rudder pedals to the NEUTRAL or fully deflected position and the yoke not fully pulled back

## Section 10 - Landing

### Descent and Landing Preparation

- Perform a long descent in the range of operating altitudes with wheels down (flap is retracted) or with the flap extended (wheels-up) at the engine conditions –

- Set the propeller to FINE PITCH, Pk = 300-340mm of Hg with preliminary heating of the cylinder head temperature not below 170°C, aircraft IAS must be 160-170km/h.  Cylinder head temperature must be kept within 160°C-180°C limits by changing the boost or opening the gills, it is determined using the indicator.  When the long-term descent is terminated, retract the undercarriage (flap) and fly according to the remaining flying mission

- Approaching the airfield, check air pressure in the main and emergency networks of the pneumatic system (pressure must be 40-50 kgf/cm²), establish two-way radio communication with ATC and on receiving clearance to descend at the airspeed indicator reading of 170-180km/h, join circuit traffic at the initial approach altitude

- Extend the undercarriage while downwind or during base to final at an indicated airspeed not exceeding 200km/h.  To extend the undercarriage, proceed as follows –

- MOVE the undercarriage lever latch to the left

- SHIFT the undercarriage lever from the NEUTRAL position to RETRACT to create counter-pressure

- SHIFT the undercarriage lever from the RETRACT position to EXTEND not retarding it to the neutral position

- CHECK the undercarriage extension by the indicator lights and mechanical indicators (three green lights of the extended undercarriage position must be on, red lights will extinguish and mechanical indicators on the wings and cowling will be out completely)

- LOCK the undercarriage lever with the help of the latch by shifting it to the right

Leave the undercarriage lever in the extend position till the aircraft taxiing in for landing and the engine shutdown.

### Planning the approach

- After undercarriage extension, maintain the indicated flying airspeed of 170-180km/h, check air pressure in the main pneumatic system and in case there is no pressure, change to the emergency system.  Perform the turn onto base leg at horizontal level flight conditions with an IAS of 180km/h

- After the turn onto base leg prior to the glide approach, check the engine temperature (in winter time the cylinder heads temperature cannot be less than 140°C), decrease the propeller pitch by shifting the propeller pitch lever fully forward and from the turn indicator reading make sure that the propeller pitch has been decreased completely

##### WARNING

Time of the engine continuous operation at rpm equal to 101% should not exceed 1 minute

- Perform the base-leg to final turn at an IAS of at least 170km/h.  Rollout of the turn must be terminated at a level of at least 150m (500ft)

- Gliding between the turn onto base leg and turn to final must be carried out at the airspeed indicator reading of 170km/h

- After rolling out of the turn to final, SET the gliding angle corresponding to the instrument speed of 150-170km/h, balance the aircraft with the help of the elevator trimmer, extend the landing split flap.  For this purpose, shift the flap lever down against the stop; make sure that the flap has been extended from illumination of red indicator light FLAP EXTENDED located on the annunciator panel

- After extension of the landing split flap, retain an IAS of 150-170km/h and at this speed perform gliding until the landing flare is initiated. It is advisable to make the approach glide, planning for a slight pulling

- Carry out improving of the calculation with an appropriate adjustment to the engine boost, maintaining an IAS of at least 150km/h.  Descent with the boost reduced must be completed prior to an altitude of 50m

- If landing preparation and planning does not provide for a safe landing, adopt a go-around procedure. During the approach, the rate of descent is not allowed to be more than 5m/s (~17ft/s)

### Going Around

- It is possible to go around from any level, including from the flare-out height.  If the pilot has taken the decision to go around, he must increase the boost up to the take-off regime by shifting the engine thrust lever to the fully-forward position during 1.5-2 seconds.  When the indicated airspeed of 150km/h has been achieved, enter a climb gradually raising the IAS and at the altitude of at least 10m retract the undercarriage (switch the lamp on, if flying at night)

- At an altitude of at least 50m, retract the landing split flap, SET the climb indicated speed of 160-170km/h and repeat approach

### Landing

- The landing flare is advisable to be started from the 5-6m altitude by a smooth moving of the yoke backwards and reducing the approach glide angle so as to approach the ground break-off at the altitude of 0.5-0.7m

- Perform holding-off during the gradual descent of the aircraft.  To do it, move the yoke smoothly backwards to provide a landing position for the aircraft such that the two-main wheels touchdown together from a height of 0.15-0.25m with the wings level and the nose wheel up

- When the two-main wheels have touched down, hold the yoke's position from when the touchdown occurred. When the aircraft has decreased speed to 110km/h, lower the nose wheel and at a speed of 80km/h, proceed to braking

- If during landing, there was no air pressure in the main pneumatic system, then after the aircraft has started a three-wheel stable landing run, open the emergency undercarriage extension lever EMERGENCY UNDERCARRIAGE and proceed to brake cautiously

- When the run is over, clear the runway, retract the landing split flap, switch the unrequired power consumers off except for the light beacon and at night, air navigation equipment.  On making sure that the brakes are proper, taxi to parking and shutdown the engine according to the advised procedure

### Crosswind Landing

- On the crosswind approach crab into the wind using a drift-correction angle

- When landing, keep in mind that the aircraft in crosswind from the left has a settling tendency

- After the two main wheels have touched down, move the rudder to obtain a coincidence between the axis of the aircraft and the runway centre line, then SET the rudder pedals to the NEUTRAL position and on lowering the nose wheel at a speed of 110km/h proceed to braking.  Compensate the aircraft downwind side banking by aileron deflection

- The touch down speed is 5-10km/h more than for usual flight

### Engine Shutdown

- Prior to the engine shutdown, switch-off the circuit breakers converter, radio altimeter, radio compass, intercommunication system, marker receiver, gyro-horizon inverter, compass system, gyro-horizon and radio station

- Cool the engine, for this purpose –

- OPEN the cowling gills and the oil radiator shutters fully

- DECELERATE the engine crankshaft speed up to 28%-34% (a fine pitch of the propeller) and run at this condition until the cylinder head temperature is reduced to 140°C-150°C

If it is impossible to cool the cylinder heads up to 140°C-150°C, then engine stopping is allowed to be performed at the cylinder head temperature not over 170°C, in so doing, note the number of cut-outs with 170°C cylinder head temperature in the engine log sheet

- After cooling the cylinder heads, carry out the engine stopping

##### CAUTION

Prior to the engine stopping, long-term idling is PROHIBITED as it causes the spark plugs to be fouled, the crankcase to be overfilled with oil and this in its turn can result in a hydraulic shock during a subsequent start

For the engine stopping, proceed as follows –

- ACCELERATE the engine up to 65%-68% with FINE PITCH of propeller during 20-30 seconds and let the spark plugs to burn-through

- DECELERATE the engine up to 28%-34% by the thrust lever

- MAKE SURE that the propeller pitch lever is SET to the position FINE PITCH

- MOVE the thrust level smoothly forwards against the stop (open fully the carburettor throttle butterfly)

- SWITCH the magneto off by setting the switch to 0 position

After stopping the engine, SET the thrust lever to the idle stop position IDLING (fully backwards) and close the fire valve.

SWITCH OFF the rest of the circuit breakers, switches and cut-outs on the switchboard.

##### CAUTION

The engine is PROHIBITED to be shutdown –

- directly from the cruise power settings and higher power settings

- by closing the fire valve with carburettor fuel usage (in order to avoid backfiring and fire)

After each flight, it is necessary to fill in a log sheet of the engine, making an appropriate entry about the engine operating time (including take-off regime) and the number of flights.

## Section 11 - Special Cases in Flight

### Pilot Actions in case of Engine Failure

- In case of an engine failure during take-off but before the aircraft rotates, immediately pull the thrust lever fully backwards and quickly apply the aircraft brakes and switch off the magnetos.  If the pilot fails to pass around obstacles, then by braking one of the undercarriage wheels turn the aircraft so as to avoid a head-on impact.  If the turn is not able to prevent against impact, close the fire valve, switch the battery off, jettison the door and retract the undercarriage

- In case of engine failure during a climb but before the turn onto the cross-wind leg, make a transition to a glide, switch the magneto, generator and battery off and land just in front of you.  While holding-off, release the door. Change the landing direction if the straight-in landing is dangerous for the crew because of an impending head-on impact

- If the CHIPS IN ENGINE light is illuminated on the instrument panel (i.e. chip appearance in the engine oil system), check the oil temperature and pressure and the engine speed via the instruments.  On making sure that the engine is operating properly, inform ATC about it and act according to his instructions, checking thoroughly the engine parameters.  If one of the parameters does not correspond to the Operating Instruction, stop fulfilment of the mission, inform ATC about it and land at the nearest airfield

### Pilot Actions in case of Pressure Drop

### Engine Failure and the Primer

This section provided courtesy of Richard Goode Aerobatics (www.russianaeros.com)

Imagine that you are flying along, and then the engine begins to run roughly, or indeed begins to stop.  It is unlikely to be electrical – i.e. a simultaneous failure of both magnetos; you haven’t felt a huge amount of vibration and therefore the engine probably hasn’t blown up; or the propeller fallen off, so quick thinking says that the problem is fuel.  So what do you do?

Following an incident where a pilot did the wrong thing, a number of Yak pilots were asked what they would do.  There is concern as to how few people know what they should do!  Also, the correct answer to this does depend on understanding the use of the primer, which all too many pilots of Yaks only regard as the device for cold-starting the engine.  In fact it serves as the emergency fuel pump, and indeed the aircraft will run on the primer alone, even if there has been a dramatic problem with the carburettor, or indeed even if the carburettor fails to work, as long as the primer is being pumped into ‘cylinder’ and air is at least getting into the engine from the carburettor.

In terms of what to do in an emergency such as this, important points are:

- First of all check the fuel pressure.  If the fuel pressure has gone down, then there is a reasonable assumption that the fuel pump has failed

- In this case steady pumping on ‘system’ will bypass the fuel pump; supply fuel to the carburettor and keep the engine going.  It might blister your hand, but you will have the breathing space to find somewhere to land

- If the fuel pressure is good, then it is a reasonable assumption that fuel is getting to the carburettor, and if you are ruling out total mechanical failure or failure of both magnetos, then the fault must be the carburettor

- In this case if the throttle is SET about half open, and then the engine primed on ‘cylinder’, but using frequent but short strokes, the engine will run reasonably well.  Clearly long strokes will alternately drown and then starve the engine (I have not done this myself, but according to those who have, it is not too difficult to establish a position that keeps the engine running reasonably)

So remember what the primer does – on the ‘system’ side it is filling and pressuring the carburettor, and it doesn’t matter how much is pumped in this way, since the excess will always return to the main fuel tank, but on the ‘cylinder’ side it is priming into the super-charger – i.e. effectively directly into the cylinders, and an excess on the ground will of course wash oil off the cylinder bores, or indeed cause a fire as excess fuel comes down through the carburettor or even out through the exhausts, while in the air the ‘cylinder’ primer can be a life saver with its ability to keep the engine going!

### Pilot Actions in case of drop in Engine Oil Pressure

- If a drop in the oil pressure in the engine is detected, check the oil temperature. If the oil temperature rises, then land immediately in the terminal area and shutdown the engine

- If flying beyond the terminal area, land at an alternate airfield or select an appropriate landing field, and then after informing ATC, perform the landing

- In the case of a forced landing, adhere to the instructions given in the section on forced landing in this operations manual and if possible, any assistance offered by ATC

### Pilot Actions in case of drop in Fuel Pressure and Non-Uniform Fuel Consumption

- Signs of fuel pressure drop can be -

- irregularities in engine operations, followed by a drop in engine rpm, some boost reduction and/or engine vibration or shaking

- drop in fuel pressure as read on the fuel pressure gauge

- In case of a fuel pressure drop, the pilot is obliged to -

- inform ATC

- turn the primer handle MOTOR PRIMING counter clockwise to the LINE position and start pumping petrol into the fuel system, checking the fuel pressure with the help of the pressure gauge

- stop fulfilment of the mission and land the airfield at the nearest alternate airfield or landing field

- if the fuel pressure on the instrument is not recovered and the engine continues to run rough, move the primer to the CYLINDER position and start manual pumping, to achieve the best possible engine conditions

- If fuel readings are low and differ significantly, bank 5°-7° towards the tank containing the least amount of fuel and continue flying until it is equal

### Pilot Actions in case of Engine Vibration

If the pilot detects unusual aircraft vibration or shaking, proceed as follows –

- in all cases (with the exception of a drop in fuel pressure) pull the thrust lever fully backwards and adopt a gliding regime, SET the appropriate flight speed

- if the shaking or vibration does not cease after this action, smoothly move the thrust lever forwards and set up the engine conditions required for horizontal flight

- if after changing the conditions the symptoms still continue, then by using the thrust lever and the propeller pitch lever, select the rpm, at which the shaking will be minimised and land on your nearest airfield or alternate airfield in this flying regime, having delivered the preliminary radio message

### Pilot Actions in case of Propeller Over-speeding

- The main signs of propeller over-speeding are –

- small engine vibrations

- an unusual increase in crankshaft rotational speed

- a significant change to the sound of the engine

- If propeller over-speeding is detected during take-off, proceed as follows –

- move the propeller pitch lever slightly backwards to increase the propeller pitch; -continue the flight not reducing boost

- at an altitude of 5-10m retract the undercarriage

- inform ATC

- make a normal circuit flight and airfield landing

- In case of propeller over-speeding during a dive, perform the following procedures –

- remove the boost fully, increase the propeller pitch

- recover the aircraft from the dive

- stop the flying mission, inform ATC and perform a normal airfield landing

### Pilot Actions in case of in-flight Fire

In case of an  in-flight fire hazard, proceed as follows –

- close the fire valve, switch the magneto and circuit breaker IGNITION off

- if possible, deliver the appropriate radio message to ATC, informing them of your aircraft location

- transition to a gliding regime and, if required, use slipping in order to provide flame-out (i.e. starve the fire)

- if the airfield landing is impossible, select a landing field and perform an off-field forced landing

- perform the off-field landing on a forced-landing area only with the wheels up and the landing split flap extended

- in the initial training version, bail-out if the landing is impossible

### Pilot Actions in case of Forced Landing

- After the decision to perform an emergency landing has been made, deliver the appropriate MAY DAY call to ATC

- In the case where the engine is inoperable, perform an airfield landing.  During approach, ensure the flap and gear is down and perform a glide at the instrument speed of 160-170km/h.  Retract the undercarriage and flap only if you are sure that planning the approach is correct

- Perform the off-field landing on an unprepared area only, with the undercarriage retracted and the landing split flap extended

- To execute the forced landing on the unprepared area, proceed as follows –

- retract the undercarriage

- close the fire valve

- switch the magneto, ignition and storage battery off

- extend the landing split flap

- at night, with poor visibility or in day time with limited visibility, switch the landing light on

- plan the approach with a small altitude excess to make a more exact analysis of slipping

- at holding-off jettison the cabin door

### Pilot Actions in case of Emergency Undercarriage Extension

- In case the pilot need to lower the undercarriage in an emergency, proceed as follows –

- deliver a radio message to ATC about the decision to perform the emergency undercarriage extension

- check for air pressure in the emergency bottle and close the valve of the main line CHARGING (in order to prevent release of air if the check valve turns out to be defective)

- SET the undercarriage lever to the NEUTRAL position

- open the EMERGENCY UNDERCARRIAGE valve for emergency undercarriage extension

- check the undercarriage extension via the illumination of the three green warning lights and mechanical indicators on each wing and the cowling

- SET the undercarriage lever to the position DOWN

- leave the valve of the emergency undercarriage extension in the open position until the flight is complete

- after the landing run, clear the runway and make sure that the brakes operate effectively.  Inform ATC and then taxi to parking

In-flight undercarriage retraction after an emergency extension is PROHIBITED.  The emergency undercarriage extension for the purposes of training should be done with counter pressure from the main system.

If the pilot fails to extend the undercarriage via the main system and via the emergency method, then land with the wheels up on a natural-surfaced runway to minimise aircraft damage.

### Pilot Actions in case of Emergency Flap Extension

In the case of an emergency extension of the landing split flap, proceed as follows –

- deliver a radio message to ATC about the decision to perform the emergency flap extension

- check the air pressure in the emergency bottle

- close the valve of the mainline CHARGING (in order to prevent the release of air if the check valve turns out to be damaged)

- open the flap lever of the emergency undercarriage extension EMERGENCY UNDERCARRIAGE

- SET the flap lever to the position EXTEND

- check extension of the landing split flap by illumination of the red warning light FLAP EXTEND on the annunciator panel

### Landing with the Flap Retracted

If the pilot does not extend the split-flap via the main or emergency method, then it is permissible to perform the landing with the flap retracted.  The instrument approach speed after turn to final must be 150-160km/h.  The landing procedure for the flap-up landing does not actually differ from the flap-down landing.  In this case, keep in mind that the gliding range, time of holding-off and touchdown speed will be somewhat more than during a flap-extended landing.

### Pilot Actions in case of Brake Failure

- In case the brakes fail while taxiing-out/taxiing-in, stop the application of brakes, inform ATC and if possible, shutdown the engine and identify the reason for the failure

- If brake failure takes place while during a ground run after landing, proceed as follows –

- when the landing run is terminated, inform ATC about the failure and clear the runway if possible

- CHECK pressure in the main air line when the aircraft is on the taxi-way and if the pressure is normal, SHUTDOWN the engine and identify the reason for the fault

### Pilot Actions in case of Radio Station Failure

- In all cases during a radio communication failure, proceed as follows –

- CHECK the plug connections of the headset cord/s; CHECK whether the radio volume control is in the position for maximum readability

- CHECK that the radio operates via other communication channels

- CHECK whether the circuit breakers (intercommunication system) and (VHF station) are not switched off

On making sure, that the radio communication system is out of order, stop fulfilment of the flying mission and land

### Pilot Actions in case of Generator Failure

- a generator failure can usually be determined by the illumination of a red warning light GENERATOR FAILURE on the annunciator panel and from readings of the ammeter.  The latter will indicate the appearance of a battery discharge

- In the case of a generator failure, proceed as follows –

- SWITCH OFF the generator

- DELIVER a radio message to ATC

- in a VFR flight, SWITCH OFF the maximum number of power consumers with the exception of the circuit breakers: IGNITION, UNDERCARRIAGE, ENGINE INSTRUMENTS, ELECTRIC TURN INDICATOR, LIGHT BEACON and at night AIR NAVIGATION EQUIPMENT

- stop the fulfilment of the flying mission and make an alternate airfield landing.  SWITCH ON the radio station transmitter or radio compass for a short time or alternately, if required

The airborne accumulator provides supply of the power consumers at night conditions during 35-40 minutes, in daytime for 50 minutes with the generator disconnected.

### Pilot Actions in case of Converter Failure

If the converter fails, the radio compass and radio altimeter are switched off simultaneously.  On having detected that the converter is damaged via an illumination of the red light FAILURE on the annunciator panel, perform the following procedures –

- SWITCH OFF the flight and navigation instruments

- CUT-OUT the circuit breakers, flight and navigation instruments

- DELIVER a radio message to ATC about the failure of the converter

Perform visual and instrument (electric turn indicator) flying, approach the airfield by radio compass and magnetic compass, and if necessary request a radio direction finder heading from ATC

### Pilot Actions in case of Speed Indicator Failure

- In case of a speed indicator failure, proceed as follows –

- inform ATC and fly towards your airfield to stop fulfilment of the flying task in an appropriate fashion,

- keep the flying regime using indications from alternate instruments and via the variometer and engine power settings (boost and rpm)

### Pilot/Crew Actions in case of a Emergency Bailout

In the initial training version, for elementary and advanced pilot training, the emergency bailout can be performed by a crewmember with the co-pilot or another pilot remaining in the aircraft.  Preliminary parachutes must be fitted whilst on the ground for all pilots.

- A forced abandonment of the aircraft by parachute is carried out –

- in cases where there is an uncontrollable fire in the aircraft

- in cases where recovery from a spin is impossible above 1000m

- if it is impossible to restore aircraft controllability

- in all cases, when the forced landing does not guarantee life safety for the crew members

Safe bailout during straight-line level flight and at glide conditions is provided up to an indicated = 220km/h.  The minimum altitude during the straight-line horizontal flight where a safe escape can be made is 150m (500ft!)

- Execution of the procedure.  The aircraft commander (who is training the pilots) gives a command “Be ready for bail-out” and the command to be executed “Abandon the aircraft”.  The crewmembers will escape from the aircraft in the following sequence –

- cadet (being trained)

- commander (trainer)

In the case of escape from an uncontrollable aircraft, only one command is given –

“Abandon the aircraft”.  During parachute separation, the latter is put into action with an automatic parachute release unit or manually with the help of a suspension ring.  The release is set to 3 seconds and to the altitude of 1000m (3,300ft)

- Actions of the crew while abandoning the aircraft (with a controllable aircraft).  Prior to escape from the controllable aircraft, achieve a straight and level flying regime and, if necessary, decrease the indicated airspeed to 220km/h.  When bailing-out from the left seat from the command “Be ready to bailout”, proceed as follows –

- DISCONNECT and remove the headset

- SET the seat to the rearmost position

- UNFASTEN the seat belts and harnesses

Upon the command “Bail-out” proceed as follows –

- JETTISON the left-side frontal door

- TAKE feet off the rudder pedals

- TURN to the left

- GRASP the front edge of the doorway with the right hand, the rear edge with the left one

- PUT the left leg on the wing, raise yourself from the seat, bend your head and separate yourself from the seat with an energetic jerk

- finding yourself on the wing, concentrate yourself and SLIP OFF the wing

When escaping from the aircraft from the right seat, perform the following procedures –

- DISCONNECT and remove the headset

- SET the seat to the rearmost position

- UNFASTEN the seat belts

- JETTISON the right-side frontal door

- TAKE feet off the rudder pedals

- TURN to the right

- GRASP the front edge of the doorway with the left hand, the rear edge with the right one

- PUT the right leg on the wing, raise yourself from the seat, bend your head and with an energetic jerk separate yourself from the seat

- finding yourself on the wing, concentrate yourself and SLIP OFF the wing

- Instructions for the crew in case of a forced emergency bailout during inverted flight, in a spin, in a dive and in a spiral.  When escaping from the aircraft in these cases, proceed as follows –

- JETTISON the door

- DISCONNECT and remove the headset

- TAKE feet off the rudder pedals

- UNFASTEN the seat belts

The escape from the aircraft in the spin or spiral should be done alternately into one door inwards the figure by means of an energetic push with arms and legs from the doorway edge and along the wing.  The bailout preparation is the same as described in the items above.

### Pilot Actions for Engine Hand Starting

CAUTION: this procedure is NOT to be attempted by inexperienced and unsupervised pilots!

Based on an experience hand-starting the M-14P with a good battery but no air.

- AFTER draining the intakes, pulling the propeller through, priming the main line pressure to 0.2 to 0.5 and priming the cylinders 6-8 times, flipping the switches and fulfilling the rest of the pre-start procedures, but BEFORE getting anywhere near the propeller, make ABSOLUTELY sure that you push in the start button and HOLD IT IN for a MINIMUM of 5 seconds (more can be better)

- TURN the master switch and magnetos OFF, drain the intakes, pull the propeller through, prime the cylinders and pull the propeller through again, switch the master instruments ON, prime the carburettor and provide 3 more shots to the cylinders, pump throttle idle-full-idle-open 1/4", ignition switch ON, start button PUSH, hold it for about 5 SECONDS, no sound, no hissing, no rotation, no clicking, nothing, then it is possible for the engine to start, magnetos ON, throttle to IDLE

LESSON: if there's fuel/air in the cylinder and the shower of sparks is cooking, it could fire at anytime with no air, no rotation and no warning. If anyone asks you to hand prop an M-14P, you both better know EXACTLY what you're doing!

DO NOT move the propeller when the engine is above 85°C.  It can be FATAL!

REMEMBER, the cylinder head temperature (CHT) can still be 100°C even 20 minutes after shutting down and the engine COULD START even with the ignition and magnetos OFF.  The best advice is to assume that the propeller is live at all times and to be cautious accordingly.

Under normal circumstances, the magneto switch should be in the 0 position until the engine starts on the sparks, then put onto both. The shower of sparks only works if you have a working battery.  If the battery is flat there is no shower. If there is no air there is no rotation.

If the battery is flat then you can only try to start with the magnetos and you might as well have both switched ON.  However, even with a full air bottle the rate of turn of the starter is seldom enough to get over the compression quick enough and the engine will usually fire BACKWARDS – not a good idea.

### Special Feature of the Power Unit at low ambient temperatures

To provide trouble-free engine operation during low ambient temperatures of +5°C and less, the power unit of the aircraft should be prepared for operation in wintertime.

## Section 12 - Operation of Systems and Equipment

### Radio Station

- The radio station is located on the instrument panel.  The pilot controls this radio station both from the left or from the right seat

- Prior to connection, the controls of the radio station should be SET to the following positions –

- The radio toggle switch NOISE SUPRESSOR to the OFF position

- the volume control to the position of maximum volume

- To switch the radio station on, proceed as follows –

- switch on the circuit breakers for the intercommunication system and the VHF on the switchboard.  After two minutes the radio station is operation, receiver noises should be heard in the earphones

- set-up the required frequency on the communication channel by using the radio control panel.  To effect transmission, push the button indicated RADIO on the yoke

- To switch the noise suppressor off, SET the toggle-switch NOISE SUPRESSOR to the position NOISE SUPRESSOR on the control panel

To switch the radio station off, SET the circuit breaker VHF to the OFF position

### Radio Compass

### General Information

The radio compass is intended to be used for automatic determination of radio bearings from radio stations and by air navigation radio compass locators and broadcasting stations, as well as for pre-landing manoeuvring and approaching.

The operating frequency range of the radio compass is from 150-1300 kHz.   Radio coverage at a flight altitude of 1000m is approximately 160km (100miles).  The radio compass is controlled from a control desk on the instrument panel from the right side and a separate instrument is used as the relative bearing indicator.  Radio compass tuning to two operating frequencies is provided.  For the fine adjustment of the receiver there are two frequency-setting controls TUNING and TUNING INDICATOR.

The switch INNER MARKER/OUTER MARKER on the instrument panel is for selecting the required operating frequency in flight and on the ground.  An aural presentation of the call signal in the headphones is given when the switch RADIO COMPASS OFF on the panel of the intercommunication system is SET to the position radio compass. The latter is supplied from a 27V aircraft d.c. electrical wiring system and from the converter 115V, 400 Hz.  Protection of the power-supply circuits is effected by circuit breakers and the radio compass mounted on the power panel.

### Pre-flight radio compass switching-in, tuning and checking

To tune and check the radio compass, proceed as follows –

- SWITCH the circuit breakers and radio compass on the power panel on

- SET the switch DIRECTION FINDER OFF on the panel to the PK position

- SET the operation mode switch on the radio compass control panel to the position AERIAL and the switch to one position or another depending on the operation mode of the ground radio station

- SET the switch INNER MARKER/OUTER MARKER on the control panel to the on position, SET the frequency of the inner marker locator with the help of a left decade tuning knob, listen to call signs and obtain a fine tuning of the radio compass with the help of the knob TUNING by a maximum deviation of the tuning indicator pointer to the right

For more accurate tuning, it is advisable to decrease the deviation of the tuning indicator pointer up to two scale divisions by using the gain control from the control desk and after tuning is complete, SET the control to the maximum position –

- perform the analogous procedures with the right tuning knob after having SET the INNER MARKER/OUTER MARKER switch to the on position

- SET the operation mode switch on the radio compass control panel to the COMP position, in this case a pointer on the radio bearing indicator on the instrument must indicate the radio bearing of the outer marker locator and the telephone sets calls of this station should be listened to

- using the LEFT-RIGHT rotatable loop control, deflect the radio bearing  indicator pointer by 45°-60° angle towards the side required

- on releasing the control, make sure that the radio bearing pointer is returned to the initial position

Make sure that the calls are being listened to correctly and the radio-bearing readings provided by the direction finder of the inner marker locator are stable.

### Radio Compass Usage in Flight

###### Flight to a Radio Station

During the radio flight, the aircraft heading is SET so that the radio bearing indicator pointer stays on the indication equal to the drift angle, and the sum of the magnetic heading and radio bearing is equal to the great-circle magnetic course that is set.  If the drift angle is unknown, then the magnetic course is selected as follows –

- by turning the aircraft, SET the radio bearing indicator pointer to zero and note the value of the magnetic course

- continue the flight, maintaining the course

- in case of changing the radio bearing by 3°-5° (this indicates the aircraft distance off track in decreasing the radio bearing to the right, in increasing to the left), perform a corrective turn of the aircraft towards the side, opposite to the drift and place the indicator pointer at a value of 6°-10° (350°-354°)

- continue the flight and observe the radio bearing variation

- if the radio bearing's variation continues, increase or decrease the heading correction by a value equal to a half of the previous correction

- the radio compass locator is marked during the fly-by by turning the radio bearing indicator 180°

###### Flight from the Radio Station

If the radio compass locator is available at the departure point or in transit of the course line, then it can be employed for the preset heading control using the radio compass.  The magnetic heading is selected in this case such that the great-circle magnetic course set is equal to the aircraft magnetic bearing.  For this, proceed as follows –

- tune the radio compass to the compass locator frequency

- place the aircraft on the desired course line with the heading SET and then calculate the aircraft magnetic bearing by a blunt edge of the radio bearing indicator pointer

- determine the heading correction

- heading correction is equal to aircraft magnetic bearing minus great-circle magnetic course set

- correct the magnetic bearing by a value of the found correction and continue the flight with the corrected heading

If the aircraft magnetic bearing is more than the great-circle magnetic course set, then the aircraft is deviated from the desired course line to the right and if less to the left.

###### Track Monitoring and Position Finding

Monitoring of track ranging is carried out by evaluating a fly-by moment of the route checkpoints, to which the known values of the side radio bearings correspond.  The magnetic bearings from the radio set are primarily transferred to the flight chart.  The designated magnetic bearings must correspond to the fly-by checkpoints.  The aircraft's location is determined using a cross-cut on the chart for the aircraft magnetic bearings from two radio stations or by a point of intersection between the radio set magnetic bearings and the actual course line.  The actual accuracy of the track ranging control and the aircraft position finding is provided, if the radio sets are placed at a distance of 100 km from the desired course line and the angle of the bearings crossing lies within 30°-150°.

###### Landing Approach Manoeuvring

Flight in terminal areas are performed according to the stated plots.  Landing approach manoeuvring by radio compass is carried out as follows –

- tune the radio compass channel MAIN to the beacon bearing frequency of channel and GUARD channel to the beacon bearing frequency of channel

- go into the beacon bearing with the magnetic heading equal or close to the landing magnetic track

- make the turn to the cross-wind leg, turn onto the downwind leg and onto base leg according to thr chart for the given airfield

- when the radio bearing = 285° (75°) make a base leg turn to the radio bearing = 0° and note the magnetic heading

- comparing the magnetic heading with the landing magnetic track, determine the aircraft position relative to the landing direction, if the magnetic heading is equal to the landing magnetic track the aircraft is located at the landing line, if the magnetic heading is more than the landing magnetic track the aircraft is to the left from the landing line and if the magnetic heading is less than the landing magnetic track, it means that the aircraft is more to the right.  If the difference between the magnetic heading and the landing magnetic track exceeds 10°, the aircraft makes a corrective turn by 15-20° towards the landing line and takes the landing course by the radio bearing indicator.  If the difference is less than 10°, the aircraft makes corrective turns by angles not exceeding 10°

- during final approach, set the magnetic heading equal to the magnetic course ± angle of drift, in this case the radio bearing will be equal to the angle of drift or 360° - angle of drift

- at the moment of the beacon bearing (channel) over-flight change the radio compass over to the guard channel, after this, the indicator pointer will show direction towards the beacon bearing channel

###### Radio Compass Switching Off

To switch the radio compass off, proceed as follows –

- set the operation mode switches on the control panel and the switch on the intercommunication subscriber's apparatus to the OFF position

- switch the circuit breakers for the APK to off

### Compass System

###### Designation

The heading system serves to determine and to indicate the heading and turn angles of the aircraft and to provide magnetic (or true) bearings, it is fitted with the complete set given below –

- Flux-gate sensor		1 pos

- Erecting mechanism		1 pos

- Console				1 pos

- Gyroscopic unit 			1 pos

- Indicator			1 pos

- Slaving unit 			1 pos

Depending on the flight conditions and the tasks to be executed, the system can operate in one of two regimes –

- magnetic slaving or

- gyro direction indicator

The main mode of operation is the gyro direction indication regime.

### Pre-Flight Compass Switching-on

To switch the compass system on prior to flight, proceed as follows –

- set the console switch NORTH-SOUTH to the NORTH position when flying in the northern hemisphere and to the SOUTH when flying in the southern hemisphere;

- set the take-off airfield latitude on the respective potentiometer on the console

- set the magnetic declination, equal to zero on the erecting mechanism

- switch the compass system power on

The readiness time of this compass system for operation in the magnetic slaving regime 5 minutes.  In 3 minutes after the power has been supplied, carry out the pre-flight checking of the compass system serviceability.

###### Pre-flight Compass System Checking

To check the compass system before the flight, perform the following procedures –

- set the MONITORING switch to the positions 0 and 300 respectively, make sure, that the compass indicator shows the indications within 0±10° and 300±10°

- set the gyro direction indicator regime and deflect the heading set switch, make sure that the movable scale is rotating

- set the slaving regime and by using the heading set switch on slave the system

###### In-flight Usage of Compass System

- Flight in the magnetic slaving operation mode

To perform flights in the magnetic slaving regime, proceed as follows –

- set zero on the erecting mechanism

- set the magnetic slaving regime

- after take-off and climbing, place the aircraft to the initial route point

- fly over the departure point on the first route leg course

- when approaching the intermediate route point, turn the aircraft by a value of the linear leading a turn to take the next route point course.  In such away fly over all the subsequent route legs

- Flight in gyro direction indicator operation mode

For flight in the directional gyro mode, proceed as follows –

- set the scale of the erecting mechanism to zero

- set the departure aerodrome latitude on the latitude scale

- set the operation mode switch to the gyro direction indicator regime

- on the line-up take-off position, if it is required, set the magnetic heading by using the heading set switch

From this point on, the compass heading indicator will show the great-circle magnetic heading relative to the departure aerodrome meridian –

- fly the aircraft to the first route leg with the great-circle magnetic heading equal to the great circle magnetic course set minus drift angle

As a result of compass instrument errors, mistakes in the determination of the drift angle and piloting can occur.  The assigned direction can be maintained with a certain angular error, this can cause a gross track error.  To reduce the distance-off-track when tracking the course, perform the following procedures –

- check the course by the indicator

- follow variation of the drift angle

- control taking the course by other air navigation aids

In flight, in order to maintain the desired course line make the heading correction, if required, so that the sum of the magnetic heading and drift angle is constantly equal to great-circle magnetic course set

- when approaching the next route leg, determine the turn angle by the formula (turn angle) = (great-circle magnetic course set of the subsequent route leg minus (great-circle magnetic course set of the subsequent route leg)

If the turn angle (LJP) has a plus sign, then make a turn to the right, if minus -to the left

- when approaching the landing airfield area (prior to climb), change the compass system over to the magnetic slaving mode and by using the heading set switch obtain slaving

- after slaving the compass system, shift it to the gyro direction indicator mode

#### NOTE

Monitoring of the compass system working in the gyro direction indicator mode is to be carried out with the help of the magnetic compass and erecting mechanism.

### Troubles and failures of the Gyro-magnetic Compass

###### Trouble, Its Signs, Crew Actions

| 1. Failure of the gyroscopic unit | A lamp GYROSCOPE TILTING lights up on the console | Use the energetic mechanism indicating the magnetic heading and a compass to determine the aircraft course |
| --- | --- | --- |
| 2. Failure of the flux-gate sensor and the erecting mechanism | Readings of the magnetic heading on the erecting mechanism and gyro magnetic heading in the straight line flight are incorrect and unstable | Use readings of the indicator when the compass system is operating in the gyro direction indicator regime, indications of the magnetic compass and indications of the instrument are employed |

### Magnetic Compass

The magnetic compass is used as a standby instrument for determination of the aircraft magnetic heading.  When using the magnetic compass it should be borne in mind that a value of residual deviation on individual courses can constitute 10°.

### Gyro-horizon

- The gyro-horizon is designed to inform the pilot about the aircraft pitch and bank angles relative to the true horizon and also about slipping direction of the aircraft

- The gyro-horizon is switched on after the engine has been started and the converter turned on. In order to switch the gyro-horizon on, cut-in the circuit breakers on the switchboard.  The gyro-horizon caging is automatic after turning the power on.  The correct gyro-horizon start is provided at pitch and bank angles at rest of ±4°

- On the line-up take-off position prior to take-off, the crew must check whether the gyro-horizon is proper and make sure that:

- the aircraft symbol on gyro-horizon indicator occupies the horizontal position and coincides with the horizon line

- while rotating the pitch angle set knob, the scale is deviating, on having checked the indicator serviceability, set the pitching scale to zero

- a red no-power warning light on the gyro-horizon is out

If one of the above mentioned requirements are not met, the take-off is PROHIBITED.  The take-off is allowed only after the gyro-horizon will get ready for operation (not earlier than in 3 minutes after its connection).

##### CAUTION

It is not permitted to use the caging button when the gyro-horizon is started and also during its normal operation on the ground and in flight.

- The gyro-horizon bank and pitch angles are 360° with the exception of pitch-up and dive angles of 85-95°.  Allowable errors in the gyro-horizon readings -

- after take-off error not more than ±3°

- errors in the bank angles indications after 360° degree turns not over ±3° (separate overshoots up to 5-6° are possible)

- errors in bank and pitch angles readings after aerobatics manoeuvring -not more than ±5°

- If in flight, the gyro-horizon provides wrong indications, it is necessary to make a transition to levelling out and push the button CAGING ONLY OF LEVEL FLIGHT placed at the horizon indicator front panel.  In this case, a caging light on the indicator illuminates and goes out when the caging is over.  Make sure that the gyro-horizon operates properly.  Further flight must be performed with special attention paid to the gyro-horizon indications that must be compared with those of the electric turn indicator and to the position nose-over and canopy front portions relative to the natural horizon.

#### NOTE

It is advisable to use the caging button at pitch angles more than +4°, as after caging the gyro erection can be switched off. Setting the circuit breaker on the switchboard to the off position turns off the gyro-horizon.

- In case of gyro-horizon failure in flight, determine the spatial attitude of the aircraft by the natural horizon and by the indicator and indications of the variometer.

Electric Turn Indicator

The electric turn indicator is designed to indicate the correct 45-degree banked turning of the aircraft in flight about a vertical axis.  It combines a turn indicator and a slip indicator in one unit. The aircraft turn is shown by the pointer and slipping by a ball.  The indication accuracy error at normal conditions of the flight with 15, 30, 45 degree banks and angular velocities 1.1°C, 2.3°C and 4°C respectively is ±1.5°.

Radio Altimeter

General Information

The radio altimeter is intended to be used for measuring absolute flight altitude in the range of 0-750m and warning that the aircraft has reached the assigned altitude, which value is preset on the indicator.  The instrument placed on the instrument panel is employed as the altitude indicator.  The instrument flange accommodates an altitude setting control with a built-in yellow warning light and a button (CHECKING) with built-in red warning light.  By rotating the ALTITUDE SET control, warning setting of the desired altitude is provided, its value is determined by a yellow triangular marker moving over the indicator scale.  When the aircraft has achieved the command altitude, the yellow light is illuminated and simultaneously a 400-Hz audio signal is applied to the pilot's telephones during 3-9 seconds.  When the CHECKING push-button is pressed, a 15±1.5m test altitude is set on the proper radio altimeter's indicator, if no button is used, the radio altimeter shows the flight absolute altitude (or H=0 on the ground).  The radio altimeter switching as well as protection of the supply circuits are provided by the altimeter circuit breaker located on the switchboard.

Radio altimeter usage in flight

- Prior to take-off

Switch the radio altimeter power on using the circuit breaker.  In this case a red light should go on and the altitude indicator point will be displaced towards a digit 750m and go beyond the scale black sector.  After radio altimeter warm-up the red light should extinguish and the indicator pointer should be set to 0±0.8 m scale division.  Using the ALTITUDE SET control, place the marker of the desired altitude warning unit against a 10m division of the scale.  Press and hold the CHECKING push button in this position.  The indicator pointer in this case will show the test altitude value of 15±1.5 m.  Release a button CHECKING, when this is done the indicator pointer will be displaced towards a zero value on the scale. When it passes a 10m division, the warning light on the altitude indicator will light up and an audio signal will be fed to the pilot's telephones.  The radio altimeter is disconnected by the switch on the switchboard.

- In flight

In flight the radio altimeter operates as follows –

- when the aircraft climbs at a level of 750m and over, the indicator pointer of the instrument goes beyond the scale black sector and it will be there until the aircraft starts to descend to an altitude of 750m.  At the moment the indicator pointer passes the marker of the assigned altitude, a yellow warning light goes on at the instrument and an audio signal will come to the telephones of the pilots

- when the aircraft climbs at a level of 1200m and more, a red warning light built-into the CHECKING control will be illuminated, it will extinguish when the aircraft descends below 1200m

- at altitudes of 750m and below the indicator pointer will show the absolute flight altitude and at a further descent the radio altimeter warns when the desired altitude will be achieved (a yellow lamp on the instrument lights on and an audio signal will be heard in the telephones during 3-9 seconds). The light illuminates until the aircraft lands and will extinguish after the power of has been off

##### CAUTION

It is not advisable to use readings when the bank and pitch angles exceed 30° -

- switch the radio altimeter off after landing

- if the radio altimeter failure Occurs in flight at a level of less than 750m, a red warning light goes on in the altimeter

- a fault signal, in this case switch the radio altimeter off

Instrument Approach Apparatus

General information

This apparatus is to be used by the homemade heating-glide path system and for International Instrument Landing System (ILS) approaches.

This system provides signals of the aircraft diversion from the heading and glide path equi-signal zones formed by the ground beacons and the inner and outer marker locators flyover warning from the radio markers signals.  The apparatus is controlled by the unit located on the instrument panel from the left.  The control unit accommodates the following controls: power switch, frequency set control with a computer, operation mode switch ILS, apparatus checking buttons.

By using the frequency set control, one can provide the operating frequency of the localizer receiver over the range of 108.1-111.9 MHz with 0.2 MHz frequency spacing. Simultaneously, tune the operating frequency of the glide-path receiver.  The marker receiver, which operates at a 75 MHz fixed frequency, is switched on in conjunction with the apparatus and has no controls.  The apparatus is fitted with built-in serviceability checking push-buttons, monitoring is carried out from the control unit.  The apparatus is supplied from a 27V DC aircraft electrical wiring system.  The power circuit is protected by the circuit breaker placed on the switchboard.

###### Apparatus pre-flight switching-on and checking

To switch the apparatus on and to check it, proceed as follows –

- switch the circuit breaker on at the switchboard

- set the power switch on the control unit to the ON position

- set the switch ILS to the position

- using the frequency set control set 110.3 MHz on the counter

- press the left CHECKING push-button. This must result in response of the heading and glide-path magnetic indicators of the instrument the heading pointer will be deflected to the left and occupy a space between 3 and 5 dots, and the glide-path pointer will go upwards and occupy the position between 3 and 5 dots. A MARKER window must be illuminated on the annunciation panel

- switch-off the apparatus by using a switch on the control unit

###### In-flight apparatus operation when the landing system is used

To provide operation of the apparatus in flight, proceed as follows –

- switch the apparatus on using the switch on the control unit

- set the ILS switch to be position

- by using the frequency set control, provide on the counter a beacon frequency of the system of the airfield where the aircraft will land

- as soon as the aircraft enters the action zone of the heading and glide path beacons on the instrument, the magnetic indicators will function and the pointers will show the aircraft diversion from the heading and glide path equi-signal zones

- while over flying the outer and inner marker locators, a MARKER will be illuminated on the annunciation panel as long pulses (dashes) and short pulses (dots) when flying over the outer and inner marker locators, respectively

- after landing, switch the apparatus off using the switch on the control unit and the circuit breaker at the switchboard

Intercommunication System

###### General Information

This system is designed to provide –

- getting on for a radio contact for the crew members by a radio set

- inter-aircraft radio communication for the crew members between each other

- capability for all crew members to listen to one radio-navigation device

- reception of two signals DANGEROUS ALTITUDE and of a marker receiver by the crew members.  Besides, aural presentation of the intercommunication signals to two additional operators is provided. Two user's sets are placed at the left and right boards of the instrument panel.  Two main connectors for connecting the airman's headset are mounted on the brackets in a zone of the door edge. The intercommunication system is supplied from 27V DC circuit

###### Use of the intercommunication system

|  | Users |
| --- | --- |
| Functional capabilities | Controls | Position | Instructor | Cadet |
| Switching-on the intercommunication power from the aircraft electrical wiring system | Circuit break of | Switchboard |  | + |
| Getting on for a radio contact | Push-button RADIO | On the yoke | + | + |
|  | Push-button INTERCOM SYSTEM | On the yoke | + | + |
| Listening to radio compass | Toggle-switch RADIO COMPASS-OFF | On the user’s apparatus | + | + |

###### Apparatus maintenance

| Power switching on |  |
| --- | --- |
| The circuit breaker of the apparatus on the cadet’s switchboard | Switch on |
| Establishing external communication by the user |  |
| 1. A push button RADIO on the yoke of a cadet or instructor | Press the push button to be engaged in communication |
| 2. RAD knob on the user’s apparatus of the cadet or instructor | Set the volume required |
| Establishing internal communication by the user |  |
| 1. A push button on the yoke of a cadet or instructor | Press the button to be engaged in communication |
| 2. A push button on the user’s apparatus of the cadet or instructor | Set the required volume of signals from the amplifier |

The apparatus provides a constant listening to the external communication signals when using the internal communication network and internal communication signals when using the external communication network with 100% loudness level.

| Listening to the radio navigation devices and special signals |
| --- |
| The switch RADIO COMPASS OFF on the user’s apparatus of the cadet or instructor | Set to position |

Signals DANGEROUS ALTITUDE and of a marker receiver are listened to with 100% volume irrespective of the controls position.

##### CAUTION

The switch (a standby one) on the user's apparatus must be always in OFF (down) position, if the user's apparatus happens to be out of order, then set this switch up to change your telephones over to other user's apparatus.

How to Use Wiper

- The wiper can be switched on when the aircraft is flying at a speed of 220km/h. It is controlled from a WIPER switch placed at the left board of the instrument panel.  The WIPER switch has four fixed positions: START, 1 SPEED, 2 SPEED, NEUTRAL (off position) and one pressed position INITIAL POSITION

- The wiper switch is turned-on using the following sequence -

- at ambient temperatures of 30 to -20°C the switch can be set to any of its positions START, 1 SPEED or 2 SPEED.  The switch operation time in flight when it is being in the START position should not exceed 5 minutes, when it is in the position I SPEED or 2 SPEED time is not limited

#### NOTE:

- If the temperature exceeds -20°C, the wiper is allowed to be directly switched on at the first or second speed

- Several double brush turns can be made during the first minute when the WIPER switch is set to 1 SPEED -64 to 90, 2 SPEED -38 to 60

- At ambient temperatures below -20°C the WIPER switch can be set to the START position for not more than 3 minutes and then it should be changed over to 1 SPEED

##### CAUTION

- At ambient temperatures below –20°C it is PROHIBITED to set the wiper switch to the 2 SPEED position

- If testing the wiper on dry glass, do not switch it on for more THAN 10s

- Switching-off the wiper from any speed is accomplished by setting the WIPER switch to the NEUTRAL position

- The wiper's brush can be returned to the initial position only after it has stopped.  The WIPER switch can be kept in the INITIAL position for not more than 2-3 seconds

### The Heating and Ventilation System

A heating and ventilation system is provided to ensure normal temperature conditions inside the aircraft's cabin.  In winter an air heater is placed in the nose section under the cowling.  A supply of hot air from the heater can be delivered to the cabin by using a control from the right-hand side of the cabin.  Hot air to the cabin is fed from the heating extension pieces mounted near to the pilot's feet. The windscreens of the cabin are heated. Switching-on of the heating system is possible both in flight and on the ground after the engine has been started.  In summer, the heater is removed and there is ventilation from the velocity head. The cabin ceiling has a rotating spindle for controlling personal ventilation of cool air.

### Aneroid and diaphragm actuated instruments and the pitot static systems

###### Description and Usage

The following instrument panel mounted aneroid and diaphragm instruments: the altimeter, speed indicator and variometer are used for measuring the flight altitude, horizontal and vertical velocities. The pilot and static pressures are applied to the instruments by means of the pilot-static tube and pilot pressure pipelines (painted in black) and static pressure pipelines (white color). The instruments are connected to the static pressure pipelines and only a velocity indicator is connected to the pitot pressure pipelines.

The pitot-static tube is mounted on the left detachable wing assembly on a special-purpose boom and is brought out forwards at a 500-mm distance from the wing leading edge to the undisturbed-flow area.  The pitot-static tube is fitted with a heating element, which is switched on using the circuit breaker, HEATING CLOCK, which is placed at the board under the middle instrument panel. The heating element of the pitot static tube is supplied from 27V-10% DC voltage.

###### Prior to flight

Set the barometric aerodrome pressure on the altimeter pressure scale according to the air traffic control data at the take-off moment.

###### Prior to take-off

Make sure, that the scale indications of the altimeter pressure scale correspond to the aerodrome atmospheric pressure.

###### In flight

- After take-off and transition climb set the barometric pressure on the altimeter pressure scale to 760mm of Hg

- If the aircraft turns out to be in a zone of rain, snow and icing, switch-on the heating of the pitot-static tube using the circuit breaker HEATING CLOCK

- In the descent mode control the vertical speed by the variometer

- On getting approach clearance, change the altimeter scale barometric pressure of 760 mm of Hg to the indication, which corresponds to the atmospheric landing airfield pressure, in the horizontal flight at the transition level.  Prior to setting the airfield pressure on the altimeter transmitted by the approach controller, compare the landing airfield pressure with that one reported in the previous weather information.  While approaching, the height keeping control is carried out by the radio altimeter

###### After Landing

Before taxiing, switch the heating of the pitot-static tube off (if it was turned on).

### Operational Limitations

- A permissible discrepancy between the barometric and atmospheric pressure scale indications at the airfield level for the altimeter is 1.5mm of Hg. Do not match the altimeter scales directly on the aircraft

- Time of the heating element continuous operation of the pitot static tube on the ground is not more than 1.5m

Failures in the pitot and static pressure feed systems and actions of pilot in case of these failures

- Clogging or icing of the static-pressure pick-up (static vents).  This trouble, providing air-tightness of the static pipe line is proper, is isolated by the following signs –

- the variometer pointer is set to the zero position and does not change with variation of the flight altitude

- the altimeter does not change its readings with variation of the flight altitude

- the speed indicator at climb will provide too low readings, and too high during at descent

###### Pilot Actions

If the altimeter, speed indicator and variometer turn out to be detective, the pilot must deliver a radio message to ATC, abort the task execution and take the course to the landing airfield by indications of the gyro-horizon and the radio altimeter.

The flight speed is controlled by the engine power settings (by readings of the pressure and vacuum gauge and tachometer).

- Clogging or icing of the pitot tube.

The main reason of the inlet port choking of the pitot-and-static tube is icing of the tube nose, which can occur as a result of the heating element failure or if the latter was not switched on. In case of pitot-and-static tube icing, clogging of its inlet port can take place and drain orifices remain open.  In this case, in the pitot-pressure chamber the pressure equal to the atmospheric one is being set and the pitot tube becomes the static-pressure pick-up.  If the inlet port of the pitot-static tube and its drain orifices get clogged, this is detected by the following signs –

- the speed indicator maintains steady-state readings and does not respond to the speed variation during the horizontal flight

- while climbing, the speed indicator readings will be increased and will decrease during descent

###### Actions of the pilot

Check whether the heating element of the pitot-static tube is switched on (the circuit breaker HEATING CLOCK, must be turned on). If in 2-3 minutes after the pitot-static tube heating has been switched on, the speed indicator readings are not restored, the pilot must inform ATC and terminate the flight and take the appropriate course towards the landing airfield.  Check the flight speed from readings of the variometer and power settings of the engine using indications of the vacuum gauge and tachometer.

### Light Facilities

###### Exterior Equipment

- The outside facility incorporates the navigation lights, a flashing beacon and a land/taxi lamp. 2. The running flights with a filament lamp and the tail navigation light with a filament lamp are mounted on the aircraft

- A red flashing light beacon with two reflector lamps is placed at the fin tip of the aircraft

- A lamp with two filaments: landing (200 W) and taxiing (130 W) ones is used as a land/taxi lamp. It is mounted on the port wing leading edge

- On the main and frontal undercarriage legs two light warning fixtures are installed to provide the extend undercarriage warning for the finisher on the ground. The type fixtures with a filament lamp are used as lights

###### Interior Equipment

- The interior light facility is designed for illumination of the instrument panel, general and local illumination of the common cockpit

- A system of red lights is employed to illuminate the instruments, sub-panels, panels and signs

- The lights are intended to be used for illumination of the instruments, sub-panels, console's panels and the instrument boards with a red light. Each lighting fixture contains two lamps.  The lighting fixture are divided in two groups: main illumination -six fixtures and emergency lighting -two fixtures

- A slot-type vertical lighting fixture serves to illuminate sub-panels, consoles and individual instruments and notices on the panels. It uses a lamp

- A lighting fixture An M is used to illuminate signs made by the light pipe method. The fixture uses a lamp

- General illumination of the common cockpit is provided with the help of a dome lamp, placed on the cockpit ceiling. A lamp is used there

- Local illumination of the cadet's (left pilot) station is carried out by a light fixture with a lamp. The illumination enables to make recordings, to use a chart and other working papers

###### Lighting facility maintenance in night flights

- Prior to the engine start, turn-on the general illumination of the cockpit and illumination of the crew instrument panel. Supply is provided from the aircraft accumulator or the airfield network

- When the engine and generator have been started, turn-on the flashing beacon running lights and the tail navigation light

- By using the adjusting rheostats, select intensity sufficient to read properly the indications of the instruments and signs

#### NOTE

Intensity of the scale lighting must not blind the pilot and produce bright dazzles on the instruments glass, on canopy and doors.

- Prior to taxiing beginning, cut-in a low light (taxiing filament) of the land/taxi lamp, where a lamp-light is used as the light source

#### NOTE

- If required, light from a landing filament (high light) can be employed, but no longer than 5m

- If day light visibility is not sufficient or limited, usage of taxiing lamps, in the day time is permissible

- Prior to take-off on the ground, switch the general illumination dome light in the cockpit off, if it was not done before taxiing. Check intensity adjustment of the instrument panel

- Before take-off beginning, change from a low light to a high one (switch the light's landing filament on)

- On gaining 100-150 altitude, switch the light off

- Adjust intensity of the instrument panel illumination, taking the eye's light adaptation to the outer light background into account (illuminated city, lead-in light)

- Use a floodlight lighting fixture when keeping records or employing the chart

- While lowering the flight level, adjust the cockpit illumination proceeding from the landing conditions (illuminated or non illuminated airfield) -

- adjust intensity of the instruments illumination

- switch the dome light off

- After turn to final at 100-150 m altitude switch the high light of the land/taxi lamp on

#### NOTE

Sometimes, when approaching (if it is raining, falling snow or dust and so on) the so-called light screen can appear when the lamps are switched on, this makes it difficult to pilot the aircraft. In this case, it is advisable to switch light of the lamps on and off recurrently and make landing at the most favourable conditions of the landing illumination for this type of weather or go to a diversion airfield.

- At the end of the landing run, switch the high light off and cut-in the low one (the taxiing filament of the lamp)

- After taxiing-in for landing switch-off the land/taxi lamp, navigation lights, flashing beacon MCA-3

- When all post-flight operations are completed, switch off the illumination of the instrument panel and general illumination of the common cockpit

- Cut-out the internal battery or ground supply

## Index

A

Aborted Flight	14

aerial	23

aerials	23

aerobatic manoeuvres	16

aerodynamic cord	12

Aeroflot	5

Aileron	12

air intake	23

Airfield Performance	14

Airplane Inspection	18

ambient temperatures	23, 30, 37

Area	12

Aspect ratio	12

B

BATTERY	17, 31

beacon	23, 33, 34, 55, 68, 74, 78, 79

blades	21, 28

boost pressure	12, 34, 38, 39, 40

bracing struts	23

braking	15, 26, 55, 56, 58

C

cabin	23, 61, 76

Cadets	15, 41

camber	21

Carburettor	13, 34, 35, 38, 39, 50

cells	23

check	17, 18, 23, 24, 26, 32, 34, 36, 38, 45, 51, 54, 58, 59, 61, 68, 69, 70, 71, 73

checked	19, 42, 43, 71

circuit breakers	31, 36, 56, 62, 66, 67, 69, 71

clamps	23

Clean	15

cockpit	24, 25, 33, 78, 79

Cooling system	11

counterweights	21

couplings	23

cowling	19, 21, 25, 34, 38, 56, 76

cracks	21

Crankshaft	12, 34, 35, 38

Crew	15, 70

Crosswind	15

Cruise	12, 13

Cubic capacity	11

cut-outs	17, 36, 56

Cylinder Head Temperature	13

D

damages	21, 22

damper	21

defects	18, 23

Dihedral	12

Dimensional Characteristics	11

door latches	24

E

elevator	23, 32, 36, 50, 51, 52, 55

Elevator	12

emergency	16, 26, 39, 40, 54, 55, 58, 60, 61, 64, 78

empty weight	15

Empty weight	11

Engine	11, 12, 32, 35, 38, 39, 50, 58

engine speed	12, 35, 38, 40, 58

Equipment	15, 66, 77, 78

F

fillets	22, 23

Filter	13

flap extension	15, 26, 61

flight logbook	18

Flight Performance	14

Flight Preparation	17

forbidden	14, 16, 38, 52, 56, 61, 71, 75

foreign objects	24

fuel consumption	12, 39

fuel level indicator	32, 39

Fuel Pressure	13

fuselage	23

G

glazing	23

Gross weight	11

Ground roll	11

Ground run	11

ground supply	79

GROUND SUPPLY	17, 31

H

hatch	23

hatches	23

Height	12

hinges	24

hub	21, 40

I

ice	17, 36

Idling	12

indicated airspeed	15, 46, 47, 48, 54, 55

Initial training	15

Inverted flight	16

L

Landing Distance	14

landing light	23, 61

Landing Run	14

leakage	21, 22, 23

Length	12, 14

Limitations	16

luggage compartment	23

M

M-14P	5, 27, 41

Magnetos	13

manoeuvres	16, 41, 52

Max engine speed	11

mixture	21

N

navigation equipment	32, 34, 55

neutral position	23, 26, 32, 33, 34, 36, 37, 38, 42, 43, 46, 47, 48, 51, 52, 54, 56, 61, 75

Nominal	12, 14, 15, 34, 37, 38

Normal cruise	11

nose	12, 21, 28, 36, 41, 42, 44, 45, 46, 48, 49, 50, 52, 55, 56, 71, 76, 77

O

Oil Consumption	13

oil contents	19

oil cooler	23

Oil Grade	13

Oil Inlet Temperature	13

oil level	19

Oil Pressure	13

oil tank	19, 27, 28

Operational Limitations	15, 77

overhauled	5

oxygen equipment	14, 39

P

parachutes	15, 16

Petrol	13, 34, 35, 38

pitot	23, 76, 77

pitot cover	23

port wing	23, 78

Preliminary Operations	17

pressure	12, 21, 22, 25, 26, 30, 31, 34, 35, 36, 38, 39, 40, 50, 54, 55, 58, 59, 61, 62, 76, 77

Propeller	14

R

radiator	23, 25, 34, 38, 56

radio compass	23, 34, 56, 62, 63, 66, 67, 68, 74

Range	11, 14

Retractable Gear	5

return flying	16

Rotation Speed	14

Rudder	12

S

seat pans	24

seats	24

Section	6, 12, 15, 17, 36, 41, 58, 66

semi-aerobatic	5

Service ceiling	11

shock-absorber	21, 22

shoulder straps	24, 25

shutter	23, 34

signal lights	21, 22

snow	17, 76, 79

Span	12

Spark Plugs	13

split flap	12, 17, 22, 26, 36, 55, 60, 61

springs	22

stalling	15, 49, 51

starboard wing	22

stem	21, 22

strut	21

supercharger	12, 28, 29

Supercharger	12, 34, 35

switches	17, 31, 36, 56

T

tail	23, 28, 78

Take-off Distance	14

Take-off Run	14

tanks	5, 32, 39

total capacity	20

Total load	15

Touch-down Velocity	14

Trainer version	15

trimmer	12, 23, 32, 36, 38, 50, 55

Tyre size	12

U

undercarriage	12, 15, 17, 21, 22, 23, 32, 33, 37, 38, 39, 54, 55, 58, 60, 61, 78

V

Variable Pitch Propeller	5

W

Weight	11, 14, 15

Wheel base	12

Wheel track	12

Wing	12, 20

wing skin	22, 23

winter	13, 17, 30, 32, 54, 76